Table of Contents bug
Dave Nadler (DRN)
# Overview
Objectives:
- Evaluate Giant Gecko
This document provides functional requirements, and outlines software constraints, design, and implementation. Also included are hardware suggestions, and wish-list for future versions.
# Document Change Log
Revision	Notes
Version 1.0, 2-August-2016	Initial notes...
Version 2.0, December-2017	Principle of operation, details on timing

# EFM32GG332F1024 - Tools
## Software Tools
Software is implemented with:
- free SiLab's Simplicity studio (Eclipse and GCC with SiLabs extensions)
- Configurator utility (within Simplicity) used for peripheral setup code generation
- open-source http://www.FreeRTOS.org/ real-time operating system
- Nope, didn't work with FreeRTOS: LUFA open-source USB stack
WARNING: Understanding and especially attempting to modify this software requires a firm understanding of asynchronous processing, synchronization, ISRs, FreeRTOS, the GCC toolchain, Eclipse, Gecko DMA/PRS, etc.
## Special Notes
Increase heap size, for example:
 Right click the project name > Properties.
1. Navigate to C/C++ Build > Settings > GNU ARM Assembler > Symbols.
2. Add __HEAP_SIZE=0x2000

## Debug
GG starter kit, configured to use on-board Segger Jlink to debug SGS board.

# Gecko Software Architecture
TBD...
## Resources
Timer2: USB subsystem (see usbconfig.h)
## SPI for DAC
USART0 SPI: 16-bit, MSB-first,
Clock active rising edge pin 42 PC9 min 18ns period nominal 50MHz freq 50%, ie 50M bits/sec
CS active-low pin 41 PC8
Bitrate?
Max supported in V4 configurator is 24,000,000 (ie, period 41.66ns, xfer time ~.75usec)
But, V4 configurator fails to generate any output! Piece of shit.
Max supported in V3 configurator is 16,000,000 (ie, period 62.5ns, xfer time ~1.1usec);
setting 16,000,00 results in much slower transfer (divisor was set to x100). Fucking buggy tools.
Manually setting clock divisor to 0 gives measured period 64ns, xfer time 686ns.
Here’s the scope photo (test task ramping DAC voltage 0-3.3v AOK):
## Clocking and Timing
### POC Phase 1
## ... uses a square wave (generated by Gecko) to toggle sensor excitation signal (the square wave is generated via a timer). During each half of the square wave:
## The edge of the square wave excites the sensor (DAC-controlled amplitude),
## After Twait, the result signal ADC measurement is initiated,
## After Tconvert, the ADC-conversion-complete triggers the ADC ISR,
## During interval TISR, the ISR absorbs the ADC reading and adjusts the feedback DAC. The feedback value required to null the ADC is the measurement result.
## Hai connected the clock to the Timer 0 DTI unit 1 output (PA4 pin 5). The desired initial clock speed is 32kHz (period 31.25 usec) Timer0 setup is as follows: - Timer 0, set to up-count, generating overflow events - Count up timer to ½ clock value (period 15.625 usec) - use CC1 to drive DT1 to drive output pin - toggle output on input overflow event - disable capture, PWM, and other fancy stuff - Set CC1 to same value as timer limit, then toggle CC1 output. Add 0 delay to CDTI1 and drive CDTI1 output pin (PA4 = pin 5). Set CC0 to ½ (or more) of timer limit, and interrupt on match. Use this interrupt to start ADC reading...
## Timer 0 -> CC1 toggle-on-match -> DTI1 -->> SGS measurement clock (PA4 = pin 5) -->> PRS#1 as a level (no edge detection) -> CC0 toggle-on-match at half-cycle -> PRS#0 pulse -> ADC conversion trigger -> CC2 capture on PRS#2 (try to record trigger polarity)
Problems with POC phase 1 attempt:
- too much work in ISRs
- difficulty with which phase is which (ADC completion ISR could be entered after clock toggled).
## Serial Data Rate