# Approximate a Circle with Cubic Bézier Curves
## Mathematics of the Bézier Curve
The general formula of a cubic Bézier curve is
bold B( t)=(1-t)^3 {bold P}_0 +3(1-t)^2 t {bold P}_1 + 3(1-t)t^2 {bold P}_2 + t^3 {bold P}_3" , "t in left[ 0";"1 right]
This is in expanded form
{bold B}(t)=left(-{bold P}_0+3{bold P}_1-3{bold P}_2+{bold P}_3 right)t^3`+`left(3{bold P}_0 -6{bold P}_1+3{bold P}_2 right)t^2`+`left(-3{bold P}_0+3{bold P}_1 right)t`+`{bold P}_0
In case of n Bézier curves for a circle, a circle arc has a central angle of %omega def { 2%pi }over n .
We only need to calculate the points for one Bézier curve. The other Bézier curves will be generated by rotation. Start point { bold P }_0 and end point { bold P }_3 of the Bèzier curve shall coincide with the circle arc. That implies
{ bold P }_0=left( 1 mline 0 right) and {bold P}_3 =left(cos{%omega}`mline`sin{%omega}right) .
The direction of the Bézier curve in its start point shall agree with the direction of the circle tangent in this point. That implies {bold P}_1=left(1 mline k right) , where the best value for parameter k has to be determined.
The direction of the Bézier curve in its end point shall agree with the direction of the circle tangent in this point. Thus the vector widevec {{bold P}_3 {bold P}_2} needs to be orthogonal to vector widevec{bold O {bold P}_3} . And because of symmetry of the arc the length of vector widevec {{bold P}_3 {bold P}_2} needs to be the same as length of vector widevec{ {bold P}_0{bold P}_1 } which is k. That implies the coordinates
{bold P}_2=left(k cdot sin{%omega}+cos{%omega}`mline`-k cdot cos{%omega}+sin{%omega} right) .
The coefficients in {bold B}(t)={bold a} t^3`+`{bold b} t^2`+`{bold c} t`+`{bold d} are then
bold a = left( 2- 2 cos{%omega}-3 sin{%omega}cdot k`mline`3 k -2 sin{%omega}+3 cos{%omega} cdot k right)
{bold b}=left(-3+3 cos{%omega}+3 sin{%omega}cdot k`mline`-6 k + 3 sin{%omega}-3 cos{%omega}cdot k right)
{bold c}=left(0`mline`3 k right) and {bold d}=left(1`mline`0 right)
Separating the coordinates in {bold B}(t) gives
B_x(t,k)= left( 2- 2 cos{%omega}-3 sin{%omega}cdot k right) t^3 + left(-3+3 cos{%omega}+3 sin{%omega}cdot k right) t^2 + 1
B_y(t,k)=left(3 k -2 sin{%omega}+3 cos{%omega} cdot k right) t^3 + left(-6 k + 3 sin{%omega}-3 cos{%omega}cdot k right) t^2 + 3 k t
## Determine the Distance of the Control Points
### General Equations
To determine the “best” value for parameter k , we consider the radial distance d between circle point and point on Bézier curve.
d(t,k)=sqrt{(B_x(t,k))^2+(B_y(t,k))^2}-1
The “classical” method is, to make the distance zero on t=0.5 . Then the Bézier curve is always outside the circle.
A different method tries to make the maximal distance for the case the Bézier curve is outside the circle same as the maximal distance for the case the Bézier curve is inside the circle.
The first derivation in t of d(t,k) has the zeros left lbrace 0, z_1=0.5-q, 0.5, z_2=0.5+q, 1 right rbrace , where d(z_1,k)=d(z_2,k) because of the symmetry. d(0,k) , d(1,k) and d(0.5,k) are minima, and d(z_1,k) and d(z_2,k) are maxima. So we are looking for a value of k , where abs{d(z_1,k)}=abs{d(0.5,k)} , or d(z_1,k)=-d(0.5,k) if considering the sign.
Such calculation needs a CAS, even if the angle %omega is a trigonometric “nice” one, like %pi/6 . You can try to get the value from a numerical calculation or from plots. I have used numerical solutions.
### Example for Twelve Bézier Curves
Using “TI- Nspire CX CAS” I get for %omega=%pi/6 the following values:
For d(z_1,k)=-d(0.5,k) I get the solution k approx 0.175535290003 .
For the “classical” approach to make d(0.5,k)=0 I get k approx 0.17553666345 .
The current (LO 6.1) value in LibreOffice is fScaledKappa =(sqrt(2)-1) cdot {4 over 3} cdot {1 over 3}approx 0.18409491661 in e.g. impCreateUnitCircle in basegfx\source\polygon\b2dpolygontools.cxx
In the following two figures the functions calculate the radial distance d(t,k) between circle arc and Bézier curve. The function f3 uses the value k approx 0.18409491661 , the function f2 uses k approx 0.17553666245 and the function f1 uses k approx 0.175535290003 .
The value used in LO 6.1 is not really bad, the radial drift is less than 0.2 percent. But the other values are much better.
Notice the scale of the value axis. For the k-values used in f1 and f2 the maximal radial drift is below dot size in usual drawings, even in 600dpi printing.
### Example for Four Bézier Curves
Using “TI- Nspire CX CAS” I get for %omega=%pi/2 the following values:
For d(z_1,k)=-d(0.5,k) I get the solution k approx 0.551915024494 .
For the “classical” approach to make d(0.5,k)=0 , I get k approx 0.552284749831 . That is fKappa in e.g. impCreateUnitCircle in basegfx\source\polygon\b2dpolygontools.cxx in LO 6.1.
For the circle in EnhancedCustomShape2d::CreateSubPath , which had used four segments in LO 6.1, k approx 0.2835 was used.
The following figures show the difference between four segments with value k approx 0.2835 as used in custom shape circles and twelve segments with value k approx 0.18409491661 as used in primitive “legacy” circles in LO 6.1. The blue lines are diameters of the circle rotated by 1 deg. The images are taken from the exported pdf-file at 800% zoom. The improvement made for bug tdf#121305 is visible.

four segments, questionable value k approx 0.2835	twelve segments, not optimal value k approx 0.18409491661

But the twelve-segment version of LO 6.1 has gaps too. They become visible in larger zoom, here 6400%.

There are no longer gaps in the twelve-segment version using the optimized k-values, here again in 6400%.