Approximate a Circle with Cubic Bézier Curves
# Mathematics of the Bézier Curve
The general formula of a cubic Bézier curve is
bold B( t)=(1-t)^3 {bold P}_0 +3(1-t)^2 t {bold P}_1 + 3(1-t)t^2 {bold P}_2 + t^3 {bold P}_3" , "t in left[ 0";"1 right]
This is in expanded form
{bold B}(t)=left(-{bold P}_0+3{bold P}_1-3{bold P}_2+{bold P}_3 right)t^3`+`left(3{bold P}_0 -6{bold P}_1+3{bold P}_2 right)t^2`+`left(-3{bold P}_0+3{bold P}_1 right)t`+`{bold P}_0
In case of n Bézier curves for a circle, a circle arc has a center angle of %omega def { 2%pi }over n .
We only need to calculate the points for a Bézier curve starting on the x‑axis. The other Bézier curves will be generated by rotation or by applying the here calculated length to a unit tangent vector. Start point { bold P }_0 and end point { bold P }_3 of the Bèzier curve shall coincide with the circle arc. That implies
{ bold P }_0=left( 1 mline 0 right) and {bold P}_3 =left(cos{%omega}`mline`sin{%omega}right) .
The direction of the Bézier curve in its start point shall agree with the direction of the circle tangent in this point. That implies {bold P}_1=left(1 mline k right) , where the best value for parameter k has to be determined.
The direction of the Bézier curve in its end point shall agree with the direction of the circle tangent in this point. Thus the vector widevec {{bold P}_3 {bold P}_2} needs to be orthogonal to vector widevec{bold O {bold P}_3} . And because of symmetry of the arc the length of vector widevec {{bold P}_3 {bold P}_2} needs to be the same as the length of vector widevec{ {bold P}_0{bold P}_1 } which is k. That implies the coordinates
{bold P}_2=left(k cdot sin{%omega}+cos{%omega}`mline`-k cdot cos{%omega}+sin{%omega} right) .
The coefficients in {bold B}(t)={bold a} t^3`+`{bold b} t^2`+`{bold c} t`+`{bold d} are then
bold a = left( 2- 2 cos{%omega}-3 sin{%omega}cdot k`mline`3 k -2 sin{%omega}+3 cos{%omega} cdot k right)
{bold b}=left(-3+3 cos{%omega}+3 sin{%omega}cdot k`mline`-6 k + 3 sin{%omega}-3 cos{%omega}cdot k right)
{bold c}=left(0`mline`3 k right) and {bold d}=left(1`mline`0 right)
Separating the coordinates in {bold B}(t) gives
B_x(t,k)= a_x t^3 + b_x t^2 + c_x cdot t + d_x= left( 2- 2 cos{%omega}-3 sin{%omega}cdot k right) t^3 + left(-3+3 cos{%omega}+3 sin{%omega}cdot k right) t^2 + 1
B_y(t,k)=a_y t^3+b_y t^2+ c_y t +d_y=left(3 k -2 sin{%omega}+3 cos{%omega} cdot k right) t^3 + left(-6 k + 3 sin{%omega}-3 cos{%omega}cdot k right) t^2 + 3 k t
# Determine the Distance k of Curve Point to its Control Point
## General Equations
To determine the “best” value for parameter k , we consider the radial distance d between circle point and point on Bézier curve.
d(t,k)=sqrt{(B_x(t,k))^2+(B_y(t,k))^2}-1
Method A: A common method is, to make the distance zero on t=0.5 . For 0<%omega<=%pi/2 the equation d( 1 over 2"," k )=0 has the positive solution k={ 4 over 3 } cdot { {sqrt{2 cdot(1-cos{%omega}) }-sin{%omega} } over { 1-cos{%omega} } } .
[Use a CAS (computer algebra system) to verify it.]
For 4 Bézier curve segments, which is %omega=%pi over 2 = 90deg , this gives k={ 4 over 3 }cdot ({sqrt 2 -1})approx 0.552284749831 .
For 8 Bézier curve segments, which is %omega=%pi over 4 = 45deg , this gives k approx 0.26521648984 .
For 12 Bézier curve segments, which is %omega=%pi over 6 = 30deg , this gives k approx 0.17553666345 .
Using this method the Bézier curve coincides with the circle arc in the start and end point and in the middle point of the arc. For all other points the Bézier curve is outside the circle.
Method B: Another method tries to make the maximal distance for the case the Bézier curve is outside the circle same as the maximal distance for the case the Bézier curve is inside the circle. I was not able to get a general solution using my CAS. For using this method you might need to restrict the calculation to the desired number of segments from the beginning.
For this method you need to calculate the values t for which d(t,k) has extrema. These are the zeros of the first derivation in t. Your CAS might fail to use d(t,k) directly because of the root. Use instead the function r(t,k)=(B_x(t,k))^2+(B_y(t,k))^2 . It has its extrema for the same values t and is numerically simpler.
In my examples I found the maximal radial distance about 25% smaller than using method A.
## Example for Twelve Bézier Curves
For %omega=%pi/6 the first derivation in t of d(t,k) has zeros left lbrace z_1, z_2 ,0 , 0.5, 1 right rbrace , where d(z_1,k)=d(z_2,k) because of the symmetry. If you plot some examples in the interesting range 0<k<1 , you can see, that it is likely, that the values d(0,k) , d(1,k) and d(0.5,k) are minima, and d(z_1,k) and d(z_2,k) are maxima. So we are looking for a value of k , where d(z_1,k)=-d(0.5,k) . A numeric solve gives solution k approx 0.175535290003 .
The version 6.1 of LibreOffice uses the value fScaledKappa =(sqrt(2)-1) cdot {4 over 3} cdot {1 over 3}approx 0.18409491661 in e.g. impCreateUnitCircle in basegfx\source\polygon\b2dpolygontools.cxx.
The following two figures show a comparison of the radial distance d(t,k) between circle arc and Bézier curve. The function f3 uses the value k approx 0.18409491661 , the function f2 uses k approx 0.17553666245 and the function f1 uses k approx 0.175535290003 .
The value used in LO 6.1 is not really bad, the maximal radial distance is less than 0.2 percent. Notice the scale of the value axis. But the other k-values are much better.
## Example for Eight BézierCurves
For %omega=%pi/4 this method gives a value of k approx 0.265205896269 . The maximal radial distance is 0.000003040488 in this case. A circle with 1m radius would have a maximal radial distance of about 0.03mm from the Bézier curve. For k approx 0.26521648984 , using method A, we would get a maximal radial distance of 0.000004246. For comparison: 600dpi means, that one dot has a width of about 0.042mm. For both values the difference would not be visible for usual drawings, neither on screen nor in print.
## Example for Four Bézier Curves
The bug tdf#121305 reports, that the approximation of a custom shape circle is bad. The test document, which I have used, has blue lines as diameters, rotated by 1deg. I have exported the drawing to a pdf-file and have used the zooming of the pdf-reader. The figure shows, that there is indeed a large gap between the custom shape outline and the ends of the diameters.
The reason was, that the custom shape circle was drawn with four Bézier curve segments with k approx 0.2835 , done in EnhancedCustomShape2d::CreateSubPath. A numeric solve of the equation d(z_1,k)=-d(0.5,k) for %omega=%pi/2 gives the solution k approx 0.551915024494 .
In a first step I have changed drawing the custom shape circle so, that it uses the same method a the “legacy” circles. Those were drawn with twelve Bézier curve segments with value k approx 0.18409491661 . That is already an improvement. But as calculated above, that is not the best k-value. And you see indeed gaps, if you use a very high zoom. There are no longer gaps visible, if one of the optimized values calculated above is used.
four segments, questionable value k approx 0.2835 / Image taken with 800% zoom.	twelve segments, not optimal value k approx 0.18409491661

The twelve-segment version of LO 6.1 has gaps too. They become visible in larger zoom, here 6400%.

There are no longer gaps in the twelve-segment version using the optimized k-values, here again in 6400% zoom.