Constants

Constant	Symbol	Value	Units
Speed of light in a vacuum	c	2.997 924 58 x 108	m/s
Permittivity of vacuum	o	8.854 187 817 620 x 10-12	F/m
Permeability of free space	µo	1.256 637 0614 x 10-6	H/m
Planck's constant	h	6.626 069 57 x 10-34	J•s
Boltzmann’s constant	k	1.380 648 8 x 10-23	J/K
Faraday’s constant	F	9.648 533 99 x 104	C/mol
Avogadro’s constant	NA	6.022 141 29 x 1023	1/mol
Unified atomic mass unit	mu	1.660 538 921 x 10-27	kg
Electronic charge	q	1.602 176 565 x 10-19	C
Rest mass of electron	me	9.109 382 15 x 10-31	kg
Mass of proton	mp	1.672 621 777 x 10-27	kg
Gravitational constant	G	6.673 84 x 10-11	Nm2/kg2
Standard gravity	gn	9.806 65	m/s2
Ice point	Tice	273.15	K
Maximum density of water		1.00 x 103	kg/m3
Density of mercury (0°C)	Hg	1.362 8 x 104	kg/m3
Gas constant	R	8.314 462 1	J/(K•mol)
Speed of sound in air (at 0°C)	cair	3.312 x 102	m/s

Imperial to metric conversions

Unit	Symbol	Equivalent	Unit
inches	in	25.4 mm/in	millimeter
mil	mil	0.0254 mm/mil	millimeter
feet	ft	0.3048 m/ft	meters
yards	yd	0.9144 m/yd	meters
miles	mi	1.6093 km/mi	kilometers
circular mil square yards pints / ounces / pounds	cir mil yd2 pt oz / lb	5.067x10-4 mm2/cir mil 0.8361 m2 / 0.5682 L/pt / 28.35 g/oz 0.4536 kg/lb	square millimeters square meters liters / grams / kilograms
calories	cal	4.184 J/cal	joules	J
horsepower	hp	745.7 W/hp	watts	W

Metric to imperial conversions

Unit	Symbol	Conversion	Unit	Symbol
millimeter	mm	0.0394 in/mm	inch	in
millimeter	mm	39.4 mil/mm	mil	mil
meters	m	3.2808 ft/m	feet	ft
meters	m	1.0936 yd/m	yard	yd
kilometers	km	0.6214 mi/km	miles	mi
square millimeters	mm2	1974 cir mil/mm2	circular mil	cir mil
square meters	m2	1.1960 yd2/ m2	square yards	yd2
liters	L	1.7600 pt/L	pints	pt
grams	g	0.0353 oz/g	ounces	oz
kilograms	kg	2.2046 lb/kg	pounds	lb
joules	J	0.239 cal/J	calories	cal
watts	W	1.341x10-3 hp/W	horsepower	hp

Conversion between codes, mV, %, and ppm

Capacitor type overview

Capacitor type	Description
C0G/NP0 / (Type 1 ceramic)	Use in signal path, filtering, low distortion, audio, and precision Limited capacitance range: 0.1 pF to 0.47 µF / Lowest temperature coefficient: ±30 ppm/°C Low-voltage coefficient / Minimal piezoelectric effect Good tolerance: ±1% to ±10% / Temperature range: –55°C to 125°C (150°C and higher) Voltage range may be limited for larger capacitance values
X7R / (Type 2 ceramic)	Use for decoupling and other applications where accuracy and low distortion are not required / X7R is an example of a type 2 ceramic capacitor / See EIA capacitor tolerance table for details on other types Capacitance range: 10 pF to 47 µF / Temperature coefficient: ±833 ppm/°C (±15% across temp range) Substantial voltage coefficient / Tolerance: ±5% to –20%/+80% Temperature range: –55°C to 125°C / Voltage range may be limited for larger capacitance values
Y5V / (Type 2 ceramic)	Use for decoupling and other applications where accuracy and low distortion are not required / Y5V is an example of a type 2 ceramic capacitor / See EIA capacitor tolerance table for details on other types Temperature coefficient: –20%/+80% across temp range Temperature range: –30°C to 85°C / Other characteristics are similar to X7R and other type 2 ceramic
Aluminum oxide electrolytic	Use for bulk decoupling and other applications where large capacitance is required / Note that electrolytic capacitors are polarized and will be damaged, if a reverse polarity connection is made / Capacitance range: 1 µF to 68,000 µF Temperature coefficient: ±30 ppm/°C Substantial voltage coefficient Tolerance: ±20% / Temperature range: –55°C to 125°C (150°C and higher) Higher ESR than other types
Tantalum electrolytic	Capacitance range: 1 µF to 150 µF / Similar to aluminum oxide but smaller size
Polypropylene film	Capacitance range: 100 pF to 10 µF / Very low voltage coefficient (low distortion) Higher cost than other types / Larger size per capacitance than other types Temperature coefficient: 2% across temp range Temperature range: –55°C to 100°C

Standard capacitance table

Standard capacitance table
1	1.1	1.2	1.3	1.5	1.6	1.8	2	2.2	2.4	2.7	3
3.3	3.6	3.9	4.3	4.7	5.1	5.6	6.2	6.8	7.5	8.2	9.1

Ceramic capacitor tolerance markings

Code	Tolerance		Code	Tolerance
B	± 0.1 pF		J	± 5%
C	± 0.25 pF		K	± 10%
D	± 0.5 pF		M	± 20%
F	± 1%		Z	+ 80%, –20%
G	± 2%

EIA capacitor tolerance markings (Type 2 capacitors)

LED forward voltage drop by color

Color	Wavelength (nm)	Voltage (approximate range)
Infrared	940-850	1.4 to 1.7
Red	660-620	1.7 to 1.9
Orange / Yellow	620-605	2 to 2.2
Green	570-525	2.1 to 3.0
Blue/White	470-430	3.4 to 3.8

Where
RT = equivalent total resistance
R1, R2, R3, …RN = component resistors

Ohm's law and voltage divider equation

AC power equation

Capacitor equations

Inductor equations

Equation for charging an RC circuit

Where
VC = voltage across the capacitor at any instant in time (t)
VS = the source voltage charging the RC circuit
t = time in Seconds
τ = RC, the time constant for charging and discharging capacitors

Equation for discharging an RC circuit

Where
VC = voltage across the capacitor at any instant in time (t)
Vi = the initial voltage of the capacitor at t = 0s
t = time in seconds
τ = RC, the time constant for charging and discharging capacitors

AC power equation

dB definitions

Examples of common gain
values and dB equivalent

Roll-off rate is the decrease in gain with frequency
Decade is a tenfold increase or decrease in frequency (from 10 Hz to 100 Hz is one decade)
Octave is the doubling or halving of frequency
(from 10 Hz to 20 Hz is one octave)

Basic op amp configurations