Functions, Menus and Settings
Version 1.70

Version 1.70.60
© Dipl.- Ing. (FH) Thomas Neumann 2000-2020

Thank you for choosing SATlive.

## Signal generator
the signal generator is located at the lower right of the SATlive window.
It features different types of signals and access to the windows mixers and level control.
Furthermore it contains eight buttons, which can be assigned to different connections, to allow quick recall of predefined routing when a ASIO I/O device driver is used. The buttons are visible only if an ASIO – device driver is selected in the Setup → I/O Devices window.
See the page Error: Reference source not found for details about the Connection – Manager.
### Set the output level
This setting is located in the signal generator area.
It controls the level of the output signal.
The values shown are attenuation values, i.e. the hottest output is reached at a setting of 0 and a value of -80 nearly mutes the output. The level settings popup menu contains some preset level values. In the web – client (see page Error: Reference source not found) you can change the volume using the control buttons (see page Error: Reference source not found).

Hints:
- Any change in the device I/O setup can cause large differences in the output level. Therefore reduce the output level when you change any audio related setting.
- The output's value can be affected by the settings in the windows output mixer. You can access the windows output mixer using the Invoke windows output mixer function in the popup of the signal generator area.
  See page 8 for details about the popup menu.
- The volume setting features a popup menu containing some predefined level values.
- The attenuation shows in values of dB.
- On the first start the level is reduced to -60dB.

### The menu of the signal-generator
This menu is assigned to the signal-generator at the lower right.
- SETUP opens the setup window assigned to the currently used signal. The signals swept sine (see page 11) and impulse (see page 13) feature a setup window.
- Output Waveform opens the selection menu to choose the waveform of the output signal (see page 10).
- Current I/O Setting shows the current settings for the audio I/O in a small window. You can also use the key-combination Ctrl – Alt – D to invoke this window.
- Open Windows Mixer for Audio Input invokes the windows settings for audio input.
- Open Windows Mixer for Audio Output opens the windows settings for audio-output.
- ConnectionManager opens the ConnectionManager window. For details refer to page Error: Reference source not found.
- ASIO driver open the setup panel assigned to the currently selected ASIO driver. See the manual of the ASIO device for details.
- Reset ASIO Driver allows you to restart the current ASIO driver if you’re facing trouble related to the driver. This does not affect the settings of the driver.
- I/O Devices opens the setup window of the I/O Audio (see page Error: Reference source not found).
- Assign Buttons for ConnectionManager opens an editor window where you can assign a connection to one of the buttons in the signal-generator area.
  Select the connection for each button from the area right to the button symbols. You can assign the same assignment to more than one button.
  The assignment varies for each ASIO device.
- Use selected Range for Bandpass this function assigns the currently selected range to the bandpass – filtered pink – noise signal.
- Direct-Reference opens the direct – reference menu described on page Error: Reference source not found.
- Freeze mutes Output: This option links the button RUNNING / FROZEN in the right menu area to the sound – generator, so that freezing the display will stop the sound – generator as well.
- Mute freezes Display: This option is available in the impulse – response display only. It links the Freeze button to the mute button. The display will freeze when you mute the output and refresh will start as soon as you’ll start the signal again.
- Reset on Start of Sound: This option links the button Sound On/Off to the button RESET in the right menu area, so that starting the sound – generator will reset the current display.
- Wav-Player: Access the control window of the wav – player. See page 16 for details.
- At the bottom you’ll find up to five settings used for the bandpass – filtered pink noise signal. Click on an entry of the list to recall the range – setting. See page 12 for details about this kind of signal.
### Frequency
This setting is located in the signal generator area and will show only if the current output signal supports different frequencies. This is true for the wave forms Sin var, Rectangle, Triangle, Sawtooth + and Sawtooth –
Set the frequency of the output signal. The arrows on the right increase/decrease the frequency in steps of 1 Hz, the left arrows in larger steps, depending on currently selected frequency. The popup menu contains some preset frequency values.
### Output signal selection
You can open this menu by clicking on the waveform label at the top of the signal – generator or via the entry Output Waveform of the menu signal – generator (see page 8.
Select the output signal from the list.
- Pink noise: MLS noise with a pink spectrum.
- Bandpass Pink Noise: Pink noise with a band – pass filter applied. See page 12 for details.
- Pink noise < 200 Hz pink noise with a high – cut at 200 Hz. Intended for measurement of subwoofers.
- Wav-File: As soon as valid audio data is present the name of the file will occur in the list. See page 16 for further details.
- White Noise: MLS noise with a white spectrum.
- 1kHz Sine wave: Sine wave with a fixed frequency of 1 kHz.
- Sin var: Sine wave with a variable frequency.
- Sweep Sine: Swept sine with variable parameters. Details on page 11.
- Sweep from High to low: Swept sine running from high to low.
- Rectangular wave: a rectangle shaped wave form with variable frequency.
- Triangular wave: a triangle shaped wave form with variable frequency.
- Sawtooth Rising: an increasing sawtooth shaped wave form with variable frequency.
- Sawtooth Falling a decreasing sawtooth shaped wave form with variable frequency.
- Impulse – creates different kinds of impulses with an adjustable repeat-rate.
  Please refer to page 13 for details.
Hints:
- You could not change the type of output signal during a MLS measurement in the impulse – response module.
- Different wave forms contain a different amount of energy. Therefore reduce the volume setting before you select another wave form.
### Swept sine (Sweep) / Sweep (Inv)
The swept sine is an output signal whose frequency increases or decrease continuously covering a given frequency range.
Select the swept sine signal in the signal generator's window from the output signal selection. The information area below the signal-type selection shows the parameters currently in use. To change the parameter, open the setup window by clicking on the information area. The sweep (Inv) signal will start at the highest frequency and run down to the lowest frequency.
#### The setup window
- Presets assigns the current settings to a preset or recall settings from a preset
- From the frequency at the start of swept sine
- To the frequency at the end of swept sine
- Duration the time in milliseconds used for one complete sequence
- Apply saves the changes and close the window
- Cancel discards the changes and close the window
Hint:
These settings do not affect the signal used for the sweep measurements in the impulse-response module.
#### Sweep Presets
In the swept sine setup window you can assign the current settings of the sweep signal to one of the four presets, or you can recall one of the presets. To invoke a preset just select it from the popup menu available in the Preset menu of the sweep setup window. To save the current settings into a preset, select the preset to store to in the sub menu Save as preset in the popup menu of the button Preset at the top of the sweep setup window.
### Bandpass – filtered Pink-Noise
The bandpass – filtered pink-noise is a signal which contains energy only in a certain range. The energy in the output signal is concentrated on that range, which is helpful in situations with high noise levels.
The red trace shows the default pink-noise signal, the blue trace a bandpass-filtered pink-noise with a range from 76Hz to 1.6kHz, with the same level setting.
#### Setting the range for the filter
There are different ways to set the filter range for the bandpass – filter used:
- Select the frequency range using the frequency – range tool (see page Error: Reference source not found) and use the Use selected Range for Bandpass entry in the popup menu of the signal – generator (see page 8).
- Select the frequency range using the frequency – range tool (see page Error: Reference source not found) and double-click on the frequency-range display below the output-signal selection.
- Choose one of the most recently used filter settings shown on the bottom of the popup menu of the signal – generator (see page 8).
### Signal Impulse
This wave – form delivers single pulses of different kind with a repeat-rate defined by the user. This kind of signals can help you to adjust delays by ear. The repeat rate covers a wide range from 1 millisecond to 60 seconds.
Like all other signals, this signal is listed in the signal-kind selection in the signal-generator area on the lower right.
Note the information below the signal – kind selection. The upper line shows the kind of impulse used, the second line informs you about the current repeat-rate.
To change the settings, simply click on this information area to open the configuration window.
#### The configuration window
This window contains two settings. The selection on the top contains the different kinds of impulse. Below you find the setting area for the repeat-rate.
There are different possibilities to change the repeat-rate
- Click on + to increase the rate by one millisecond.
- Click on – to decrease the rate by one millisecond.
- Hold down the Shift key and click on + to increase the rate by ten milliseconds.
- Hold down the Shift key and click on – to decrease the rate by ten milliseconds.
- Hold down the Ctrl key and click on + to increase the rate by 100 milliseconds.
- Hold down the Ctrl key and click on – to decrease the rate by 100 milliseconds.
- Click on the value with the left mouse-button or on the whole area with the right mouse-button to open a popup menu which contains some preset values.
#### Available Impulses
There are different kinds of impulses available for this signal. The green line shows the unaffected signal and the blue line shows the signal looped back.

- Single
  Just a needle with a size of one sample, heading upwards.
- Single (Sym)
  A needle heading upwards immediately followed by a needle heading downwards.
- Step
  A needle heading upwards, followed by a zero and a needle heading downwards.
- Sine
  The positive half of a 6 kHz sine wave.
- Sine (sym)
  One full cycle of a 6kHz sine wave.
- Sine (long)
  The positive cycle of a 1kHz sine wave.
  Please note that in the picture the scaling of the x - axis differs from the pictures above.
- Sine (long, sym)
  A full cycle of a 1kHz sine wave.
  This impulse is the one that 'sounds' best, so you should prefer it.
### The WAV – Player
SATlive features a simple wav – player. This player will play audiofiles which feature the wav (windows pcm audio) format.
It will always put out a mono signal.
The samplerate of both, the file and SATlive must match.
#### The control window of the Wav – Player
Use the entry Wav-Player in the signal – generator’s menu (see page 8) to open this window.
If you’ve selected a valid audio – file then the full name and some properties of the file will show in the upper area of the window.
Use the selection Audio Track to choose the source for the mono signal.
Beside of using only one of the channels you can also use an average of both channels by selecting the entry Sum L and R.
The button Select File will open a file – selection dialog where you can choose the audio file you want to use.
The button OK will close the window.
As soon as a valid file is selected it’s name will occur in the signal – type selection.
Hints
- The length of the audio data is limited to 10 minutes. If the length of the data in the file exceeds that limit, then the audio data is truncated to the first 10 minutes.
- The audio data will loop.
- A mismatch of the samplerate will cause a warning message in the upper area.
### VU Meter
The VU Meter is located in upper right area of the SATlive window.
It shows the levels of both inputs.
The bar – graph display shows the input levels related to digital full-scale.
The peak level is indicated by a single line, and the RMS value is shown as a solid bar.

Hints:
- You can use any signal, either external or from the internal signal generator to adjust the input level.
- The input level is adjusted in the windows recording mixer, which can be accessed using the Open Windows Mixer for Input function in the popup menu of the signal-generator area. See page 8 for more information about this popup menu.
- In the MAT module you can select the input for display by clicking on the labels below the bar – graph display. See page Error: Reference source not found for details.
- You can set the fall-back time of the peak display in the Setup Level Display window. See page Error: Reference source not found for details.
- Avoid clipping the input to assure good quality of the results. SATlive will stop the calculation if either clipping occurs or the input – level is too low.
### Start the output signal
This function is located in the signal generator area.
It is located right of the output level setting.
The current state of the signal generator is indicated by the color of the vertical line left of the speaker – icon. Green indicates the signal – generator putting out a signal, while a red line indicates that the output is muted.
Hints:
- You could not mute the output during a MLS measurement.
- You can also use the shortcut G to toggle the state of the output.
- When the signal – generator (see page 6) is stopped, then the short – cut Shift – G will start the sound and reset the averages.
- The option Freeze mutes Output in the menu links the control of the output with the control of the display so that freezing the display will mute the output also.
- All measurements in the impulse – response module control the output. You control this behavior for the MIR – measurement (see page Error: Reference source not found) in its setup – window.
### Level Display
The level display is located at the top of the VU Meter.
It shows the average level (RMS) of the mic input. You can set the time used for averaging in the Level Display's setup window.
You can use a Weighting Filter for this display. The selection of the weighting filter is in the Level Display's setup window. The currently selected Weighting Filter is indicated by a letter in the label shown below the number.
Furthermore the display can show the crest factor of the signal applied to the mic input.
- dB(A) the Weighting Filter A is currently selected.
- dB(C) the Weighting Filter C is currently selected.
- dB(Crest) the result shows the crest factor, which is the difference between peak and rms level.
- dB no Weighting Filter is currently used.
To open the Level Display setup window, described on page Error: Reference source not found, click on the level – display area.
## The Tracemanager
You can use the tracemanager to display and average saved frequency responses.
To invoke the Tracemanager either click on the button Tracemanager or use the shortcut Ctrl + T.
During the measurement of the impedance trace (see page Error: Reference source not found) you can use the tracemanager to show amplitude responses in the background.
### Single traces
The upper part of the tracemanager window contains eight similar areas. Each area can handle one trace.
This function are available in any of the eight areas:
The upper line shows the name of the trace. The rectangle at the left will show the color used for drawing as long as the option Weighting affects Color had not been activated in Setup → Measurement (see page Error: Reference source not found).
Otherwise the color used for drawing is controlled by the weighting assigned to the trace and the rectangle will show no color.
This area also contains a popup menu, described on page 21.
- Load Trace open a saved frequency response. The popup menu of trace name display contains a list of the most recent used files where you can pick a file with a double click.
- Show Trace displays the loaded trace.
  This option is enabled only if a valid trace is loaded.
- Average Trace to result averages the loaded trace to the master trace using the weighting selected. This function is enabled only if a trace is loaded and the loaded trace has the same samplerate as the master trace.
- Set Offset, Smoothing, Color open a window containing additional settings like offset or color. See page 24 for further information.
- Weighting the colored field right of file name display shows the currently selected weighting of the trace. Toggle the three different weightings with a mouse-click on this field.
  The trace width used for the display of the trace is changed according to the selected weighting and the trace width assigned to this setting (see page 26 for details).
  If you’ve activated the option Weighting affects Color in Setup → Measurement (see page Error: Reference source not found) then the trace will draw using the color assigned to its current weighting. Otherwise the color assigned to the trace will be used.
  See page 25 for further details about using different weightings.
#### The popup menu of the trace – name display area
This popup menu is assigned to each single – trace section (see page 20) of the tracemanager. To access this menu click on the trace – name section using the right mouse – button.
- Set Offset, Smoothing, Color: open a window containing additional settings like offset or color. See page 24 for further information.
- Clear single trace removes this trace from the tracemanager.
  The trace itself is not affected.
- File Info opens the File – Info window, described on page Error: Reference source not found.
- Load Trace: open a saved frequency response.
- Load from Project use this entry to import a trace contained in the current project.
- File list the file list shows the recently used files. To load a file from the list, just click on the name of the file in the menu.
If no trace is currently loaded, then only the entries Load trace, Load from Project and the file list will be available in this menu.
### Master Trace
In the tracemanager the Master Trace represents the result of the averaging of the traces selected for averaging.
The following functions are available for the master – trace:
- Save the master – trace trace to a file.
- Show the master – trace in the trace display window.
- Invert the master trace mirror the master – trace's display on the 0 dB line to ease the adjustment of equalizers.
- Color of the master trace.
- Reset Averaging click on this button to reset the average to main-trace button of each trace to false.
- The list below the buttons shows the names of the traces currently averaged.
### Global functions
- The button Delete will remove all traces from the tracemanger. To clear a single trace use the entry Clear Single Trace in the popup menu assigned to the display of the trace’s name.
- Use the menu to import all eight traces at a time. See page 23 for further information about the import menu.

### The menu Import
Using this menu you can import up to eight traces simultaneously into the tracemanager (see page 20).
- Copy current QuickTraces will import the quick-traces currently used.
- Copy from project will import the quick-traces assigned to a certain speaker in the current project. Therefore a window will show where you can choose the speaker whose traces you want to import.
  In case that the project contains just one speaker a confirmation box will show instead of the selection window.
- Copy from an other project will open the file – selection dialog (see page Error: Reference source not found) where you have to choose the project first. After that the import will continue as described above for the Copy from Project entry.
- Do not clear empty traces if this option is selected then a traces previously assigned will remain if there is no valid trace to replace it. Otherwise all previously assigned trace will be cleared before the start of the import.
Hint
Each trace will keep its location during the import.
This means that for example the Quicktrace 5 will always import to trace 5, no matter if there are other valid traces or not.
### Offset, Color and Smoothing
This window contains additional settings for the traces displayed using the tracemanger (see page 20).
- On the upper left you can find the control of the vertical position of the trace. It operates in the same way as the offset control in the main window, which is described on page Error: Reference source not found of this document.
- The colored rectangle on the upper right indicates the color currently assigned to this trace. Click on it to open the color – selection dialog where you can choose the desired color.
  Please note that the option Weighting affects Color in Setup → Measurement (see page Error: Reference source not found) will link the color of the display to the weighting of the trace, using the colors set in the Setup → Weighting (see page 26) section.
  In this case the label left to the trace in the tracemanager name will stay blank, while otherwise it will show the color of the trace.
- Smoothing select the smoothing of the trace.
- Display Coherence this setting is enabled only if the trace contains coherence information. This is true only for traces saved in the Transfer Function measurement in the MAT module. This option determines if the coherence trace related to this trace is shown or not.
- Show trace enables you to control the visibility of the trace.

Hints:
- The changes are displayed in real-time.
- If you exit this window using the Cancel button then all changes will be lost, and the display switches back to the old settings. To keep the changes, exit this window using the OK button.
### Weighting and averaging
The tracemanager enables you to average up to eight traces using different weightings.
There are three levels of weighting available. You can edit the parameter for the weighting at Setup → Measurement (see page Error: Reference source not found)
If different traces are averaged in the tracemanager they are weighted according to their levels of weighting.
#### Example
Averaging of two traces using the following levels of weighting:
Primary location: 10
Secondary location: 4
Tertiary location: 1
Both traces with the same level (primary).

One trace primary, other secondary.

One trace primary, other tertiary.
#### Using Averaging
The proper selection of the mic's locations for measurement has a great influence on the measurement's result.
You can take the following as a rule of thumb:
- One primary location for every speaker, located on axis in speaker's direct sound range.
- Additionally one or more secondary locations in direct sound range, but off axis.
- Tertiary locations are used to check for coverage or interaction with other speakers.
- The creation of the master trace for setting the EQ should be based mainly on the primary location. Secondary locations are used to check if a peak or dip is a result of the mic's location, or a common problem in the whole coverage area.
- Tertiary location are mainly used for special tasks like delay alignment or level adjustment, but normally not as a base for the adjustment of the equalizer.
### Setup Weighting
These settings are located in the Setup → Measurement window. See page Error: Reference source not found for details.
Set the parameters for three levels of weighting for traces averaged in the tracemanager.
- The Names of the three levels are given by the software. Levels are labeled primary location, secondary location and tertiary location.
- Weighting set how much the trace influences the result. As higher the value, as higher the influence. See page 25 for details.
- Trace Width select the width used to display a trace with this weighting.
- Color set the color used for the weighting indicator in the tracemanager. See the tracemanager section starting at the page 20 for further details.
- If you activate the setting Weighting affects color then the traces of the tracemanger will draw using the color assigned to the current weighting of the trace.