### Cursor Menu (FFT and MAT)
This menu is located right in the lower menu bar.

(Simple menu layout)

(Complex menu layout)

- Range open the range sub menu where you can select the displayed frequency range. See page 3 for details.
- Cursor on Peak move the cursor to the current peak of amplitude response. The shortcut is Shift-P.
- Lock on Peak perform the Cursor on Peak function every time a new trace is drawn. In order to reset this option click again on the button or perform an other cursor related operation (Cursor on Peak, mouse click on the trace to set the cursor, movement of the cursor using arrow keys on your keyboard). The function's shortcut is P.
Hint:
You can use the shortcut C to hide/show the cursor.
### Gain / Offset Setting
This setting is located at right window. It is available in the MAT module and in the FFT module. Changing this value moves the selected trace up or down in the display window. You can use this setting to center the selected trace or to shift it in order to compare it to another trace. You can use the mouse to move the selected trace up or down, if the option Allow Gain-Setup using Mouse option is activated in the popup menu of the value display or in the Tools menu.
Hints:
- Use the shortcut Z or a double-click on the gain display to set the gain to zero.
- Use Center Trace or the shortcut M to adjust the gain to center the live trace in the display area.
- The gain settings affects the amplitude read out. Therefore SATlive shows the current gain setting behind the amplitudes value, if the gain is differs from zero.
- The colors of the display are swapped to indicate an offset value different from zero.
- Use the shortcuts Page Up and Page Down to change the offset.
- The area displays the label and the color of the selected trace.
  To open the selection menu, click on the name or on the color.
  See page Error: Reference source not found for details about selected traces. Please note, that not all measurements will support selected traces.
- The value-display area contains a popup menu where you can select some predefined offset settings and where you can enable the movement of the selected trace by moving the mouse vertically with the left mouse-button holded down using the Allow Gain – Setup using Mouse entry.
- When working with the Live – Add Trace or the Perfect – Addition Trace (see page Error: Reference source not found) you can use the entries in the pop-up menu of the cursor-info area in the right-menu bar to determine whether the offset should affect the calculated trace(s) or not.
### Display range selection
The Range selection is located in the lower menu bar.
Use it to select the visible frequency range for the display.
Beside the three ranges Low, Mid and High you can select a fourth setting, which is called User.
You can change the border of the user setting either (like the borders of the three other settings) at Setup → Post Process or by assigning the currently used borders using the Assign current range option.
The Full range function restores the full frequency range.
If a transfer measurement is performed in the MAT module then this menu contains the Linear Scaling (X-Axis) option, which activates a linear scaling of the frequency axis, opposite to the commonly used logarithmic scaling. The linear scaling might be helpful when you work with the phase trace.
Logarithmic (default) frequency scale	Linear frequency scale

You can also use the right mouse button to select the frequency range you want. Just move the cursor to one end of the desired range, click and hold down the right mouse button. Now you can select the frequency range by moving the mouse to the right or to the left. A dashed rectangle marks the current selection. The display changes to the new values as soon as you release the right mouse button.
### Show Range at Cursor
You'll find this setting in the popup menu of the trace display in the FFT and MAT module.
This option shows two lines with the selected distance related to the amplitude value at the current cursor position.
If you’ve enabled the Pink spectrum lines option in Setup → Display (see page Error: Reference source not found) then the grid will contain lines showing the -3dB slope.
The horizontal grid option shows a horizontal line at the cursor's intersection with the selected trace.
Hints:
- The cursor always shows the values of the currently selected trace.
- You can select the trace to analyze in the popup menu of the trace display using the Show Values of option.
### The popup menu assigned to the trace display
Open this menu by clicking on the trace – display window with the right mouse button or by pressing the key J on your keyboard. The content of this menu varies dependent on the current status and the measurement selected.
- Show values of select the trace whose values are shown. See page Error: Reference source not found for details.
- Group-delay related to select the reference time used for the calculation of the group-delay. This option is available only in the impulse response's FFT module.
- Invert live trace flip the live trace on the zero dB line. The shortcut is Shift + I.
- Full trace display show the whole valid frequency range. The shortcut is F.
- Information show information about the currently selected trace.
- Show Range at Cursor draws horizontal guide lines related to the value at the cursor's current position.
- Delay = Cursor applies the delay value at the cursor's current position to the current delay. This option is enabled only in the impulse-response measurement. You can also use the shortcut F3 to invoke this function.
- Marker open the Menu Marker. See page Error: Reference source not found for details.
- Tools invoke the Tools menu (see page Error: Reference source not found).
- Layout opens the layout-sub menu. See page Error: Reference source not found for details.
- Open Delay Finder open the delay-finder window. Available in the MAT module only. See the delay-finder section on page Error: Reference source not found for details.
- Low-Frequency Delay-Finder executes the Low-Frequency Delay calculation tool. See page Error: Reference source not found for details.
- Addition of Signals open the menu for the addition of signals tool.
- Show Virtual EQ show or hide the Virtual EQ’s trace. See page Error: Reference source not found for details.
- Target Amplitude shows/hides the Target Amplitude. See page 12 for details.
### Smoothing
This selection is located on left side in the lower menu bar.
Select the amount of smoothing applied to the live trace.
The value of a point for the display is calculated as the mean value of the selected range.
If, for example a range of one octave is selected, then the mean value is calculated from the frequency of the current point minus half an octave to the frequency of the current point plus half an octave.
Using the unit octave is closer to human hearing as a fixed frequency range or a fixed amount of points.
The option Similar to Ear varies the width of the smoothing depending on the frequency. The higher the frequency, the smaller the window (in octaves).
Hint:
Human hearing is very sensitive to peaks in frequency response so you should not apply too much smoothing.
### Show Values of
- This selection is located at trace display's popup menu.
- Select the trace to read values from. You can select any trace which is visible.
- Just choose the trace you want from the sub-menu.
- The selected trace is indicated in front of the values.
- You can use the shortcut T to toggle the cursor readout.
### Value Editor Field
This edit field is located right of the layout – parameter selection below the trace display in FFT and MAT module.
This field shows the current value of the selected layout parameter.
You can change this value by:
- The selection of a preset value from the field's popup menu.
- Clicking on the arrows on the right side of the field.
- A popup menu containing some preset values is available for all settings.
SATlive shows the name of the selected parameter left of the value edit field.
See the page Error: Reference source not found for a description of the parameters available.
### Frequency Range Tool
The frequency – range tool is available in the MAT module and in the FFT module.
This tool allows you to select a horizontal range and will display its properties. See page 10 for more information about the values shown. The menu (see page 11) allows the configuration of the value display and of the selection. You can use the range selected also in this functions:
Bandpass – filtered – pink noise (see page Error: Reference source not found).
- Delay – suggestion tool (see page Error: Reference source not found).
- Low – frequency delay – finder (see page Error: Reference source not found).
- Target – amp line (see page Error: Reference source not found).
#### Operation
The frequency – range tool features three states. Use one of this option to proceed to the next state:
- Press the key D on your keyboard.
- Hold down the left mouse button and click with the right mouse button.
- Click on the range – step icon at the left.
- Click on the top entry in the menu of the frequency – range tool (see page 11).
#### State 1: No range selected
In this step there is no frequency range marked or available. Move the cursor to the desired position of the latched cursor. Please note that the function of the latched cursor depends on the currently selected mode. See page 11 for details.
Proceeding to state 2 will set the latched cursor to the current position of the cursor.

#### State 2: Mark the range
In state 2 you can mark the range. This can be done by moving the cursor with the left mouse button down, by using the left and right arrow keys on your keyboard or by clicking on the desired position.
In state 2 you can, in addition to the options mentioned on page 8, use this options to proceed to step 3:
- Move the mouse outside the trace – display area.
- If you've activated the option Unlock Cursor on Button Release in the menu (see page 11) then the state will change to step 3 as soon as you release the left mouse button for the first time.
#### State 3: Range fixed
In state three the range remains marked while moving the cursor will not change the range marked.
To clear the range just proceed as described on page 8. Doing so will reset to
state 1 (see page 8).
In any state the key – combination Shift – D will immediately reset to state 1.

#### Information displayed
The information of the cursor range tool is shown on the left of the information area above the trace display.
- Latched Cursor the position of the latched cursor. This is the position of the cursor at the moment when you proceed to state 2 of the frequency range tool. See page 8 for details.
- Center frequency of the range. The position is shown as a dashed line in the trace display. Depending on the settings in the menu (see page 11) this value might be the same as the selected cursor.
- Selected Range the third line shows both borders of the currently selected range. With the mode set to Latch Cursor is Border in the menu (see page 11), one border frequency is the same as the frequency of the latched cursor.
- The bottom line contains information related to the width of the selected range. Use the menu (see page 11) to select the value(s) you want to see:
  - BW the range between both positions related to the center-frequency[1].
    [1] This is not the correct definition of the Bandwidth, but it's the Bandwidth definition used in many digital equipment.
  - Q Quality, calculated by 1/BW.
  - Octaves bandwidth in octaves.
  If the option Show Values at Main Position is selected in the menu (see page 11), than the information related to the current cursor-position is shown here.
- An icon left to the bottom line indicates the selection – mode currently set in the menu (see page 11):
  - Latched Cursor is Center Frequency:
  - Latched Cursor is Border:
#### The menu of the frequency – range tool.
To invoke this menu just click on the arrow symbol in the upper left corner of the info area above the trace display.
The topmost entry will proceed to the next step of the frequency – range tool. See page 8 for details.
Select range of interaction: Selects the frequency – range with a level – difference below the second threshold of the interaction – area tool (see page Error: Reference source not found), starting at the current position of the cursor. This entry will show a popup menu where you can choose the second trace. The next menu entry will invoke this function using the trace listed here.
- The next two entries define the use of the latched cursor in the calculation of the frequency – range. The key W on your keyboard will toggle both modes.
  - Latched Cursor is Center Frequency: the latched cursor will mark the center – frequency. The second border will be calculated based on the position of the cursor.
  - Latched Cursor is Border: the latched cursor marks one border of the frequency – range. The center – frequency will be calculated based on the position of the cursor.
- Use selected range for bandpass will assign the current range to the signal bandpass pink noise. See page Error: Reference source not found for details about this signal.
- The next three entries allow you to set the display the bandwidth. See the information – display section on page 10 for details.
- The Show values at main position option flips the display position of the data of the current cursor and the information to the selected range.
- The Unlock Cursor on Release of Button with this entry checked the state of the frequency – range (see page 8) will changes from state 2 to state 3 as soon as you release the left mouse – button.
- Use the next three entries to limit the frequency range displayed.
- You'll find a list of previously used ranges at the bottom of the menu.
### Target Amplitude
You can show a target amplitude line in the transfer-function measurement.
This line serves as a guide line for EQ and level adjustments. This line is also used as border for the shadow – fill.
If the target – amplitude shows, all level readings relate to the position of the target – amplitude.
#### Controlling the Target Amplitude
To set the target – amp line, just move the mouse onto the info area on top of the trace display, hold down the left mouse button and move the mouse downwards until you reach the desired position.
To move the target – amp line grab the handle on the left and move it with the left mouse button pressed.

Use the entry Target Amplitude in the popup menu assigned to the display area or the shortcut U to hide/show the target–amp line, and the menu Target Amplitude (see page Error: Reference source not found) to control the target amp line.