# Material Handling Equipment
Material handling equipment (MHE) is used for the movement and storage of material within a facility or at a site. MHE can be classified into the following five major categories:
Transport Equipment. Equipment used to move material from one location to another (e.g., between workplaces, between a loading dock and a storage area, etc.). The major subcategories of transport equipment are conveyors, cranes, and industrial trucks. Material can also be transported manually using no equipment.
Positioning Equipment. Equipment used to handle material at a single location so that it is in the correct position for subsequent handling, machining, transport, or storage. Unlike transport equipment, positioning equipment is usually used for handling at a single workplace. Material can also be positioned manually using no equipment.
Unit Load Formation Equipment. Equipment used to restrict materials so that they maintain their integrity when handled a single load during transport and for storage. If materials are self-restraining (e.g., a single part or interlocking parts), then they can be formed into a unit load with no equipment.
Storage Equipment. Equipment used for holding or buffering materials over a period of time. Some storage equipment may include the transport of materials (e.g., the S/R machines of an AS/RS, or storage carousels). If materials are block stacked directly on the floor, then no storage equipment is required.
Identification and Control Equipment. Equipment used to collect and communicate the information that is used to coordinate the flow of materials within a facility and between a facility and its suppliers and customers. The identification of materials and associated control can be performed manually with no specialized equipment.
| Top | About MHE Taxonomy |

## I. Transport Equipment
### A. Conveyors
Chute conveyor / Wheel conveyor / Roller conveyor / Chain conveyor / Slat conveyor / Flat belt conveyor / Magnetic belt conveyor / Troughed belt conveyor / Bucket conveyor / Vibrating conveyor	Screw conveyor / Pneumatic conveyor / Vertical conveyor / Cart-on-track conveyor / Tow conveyor / Trolley conveyor / Power-and-free conveyor / Monorail / Sortation conveyor

### B. Cranes
Jib crane / Bridge crane / Gantry crane / Stacker crane

### C. Industrial Trucks
Hand truck / Pallet jack / Walkie stacker / Pallet truck / Platform truck / Counterbalanced lift truck / Narrow-aisle straddle truck	Narrow-aisle reach truck / Turret truck / Order picker / Sideloader / Tractor-trailer / Personnel and burden carrier / Automatic guided vehicle (AGV)

### D. No Equipment
_
## II. Positioning Equipment
Manual (no equipment) / Lift/tilt/turn table / Dock leveler / Ball transfer table / Rotary index table / Parts feeder	Air film device / Hoist / Balancer / Manipulator / Industrial robot

## III. Unit Load Formation Equipment
Self-restraining (no equipment) / Pallets / Skids / Slipsheets / Tote pans / Pallet boxes/skid boxes / Bins/baskets/racks / Cartons	Bags / Bulk load containers / Crates / Intermodal containers / Strapping/tape/glue / Shrink-wrap/stretch-wrap / Palletizers

## IV. Storage Equipment
Block stacking (no equipment) / Selective pallet rack / Drive-through rack / Drive-in rack / Flow-through rack / Push-back rack / Sliding rack	Cantilever rack / Stacking frame / Shelves/bins/drawers / Storage carousel / Automatic storage/retrieval systems (AS/RS) / Split case order picking system / Mezzanine

## V. Identification and Communication Equipment
Manual (no equipment) / Bar codes / Radio frequency (RF) tag / Magnetic stripe	Machine vision / Portable data terminal / Electronic data interchange (EDI)/Internet

## I-A. Conveyors
Conveyors are used to move materials over a fixed path. The major types of conveyors are:
Chute conveyor / Wheel conveyor / Roller conveyor / Gravity roller conveyor / Live (powered) roller conveyor / Chain conveyor / Slat conveyor / Flat belt conveyor / Magnetic belt conveyor / Troughed belt conveyor / Bucket conveyor / Vibrating conveyor / Screw conveyor / Pneumatic conveyor / Dilute-phase pneumatic conveyor / Carrier-system pneumatic conveyor	Vertical conveyor / Vertical lift conveyor / Reciprocating vertical conveyor / Cart-on-track conveyor / Tow conveyor / Trolley conveyor / Power-and-free conveyor / Monorail / Sortation conveyor / Diverter / Pop-up device / Sliding shoe device / Tilting device / Cross-belt transfer device

Conveyors are used:
- When material is to be moved frequently between specific points
- To move materials over a fixed path
- When there is a sufficient flow volume to justify the fixed conveyor investment
Conveyors can be classified in different ways:
- Type of product being handled: unit load or bulk load
- Location of the conveyor: overhead, on-floor, or in-floor
- Whether or not loads can accumulate on the conveyor
### 1. Chute Conveyor
Unit/Bulk + On-Floor + Accumulate
Inexpensive
Used to link two handling devices
Used to provide accumulation in shipping areas
Used to convey items between floors
Difficult to control position of the items

### 2. Wheel Conveyor
Unit + On-Floor + Accumulate
Uses a series of skatewheels mounted on a shaft (or axle), where spacing of the wheels is dependent on the load being transported
Slope for gravity movement depends on load weight
More economical than the roller conveyor
For light-duty applications
Flexible, expandable versions available
### 3. Roller Conveyor
Unit + On-Floor + Accumulate
May be powered (or live) or nonpowered (or gravity)
Materials must have a rigid riding surface
Minimum of three rollers must support smallest loads at all times
Tapered rollers on curves used to maintain load orientation
#### 3(a) Gravity Roller Conveyor
Alternative to wheel conveyor
For heavy-duty applications
Slope for gravity movement depends on load weight
For accumulating loads
#### 3(b) Live (Powered) Roller Conveyor
Belt or chain driven
Force-sensitive transmission can be used to disengage rollers for accumulation
For accumulating loads and merging/sorting operations
Provides limited incline movement capabilities
### 4. Chain Conveyor
Unit + In-/On-Floor + No Accumulate
Uses one or more endless chains on which loads are carried directly
Parallel chain configuration used to transport pallets
Vertical chain conveyor used for continuous high-frequency vertical transfers (cf. vertical conveyor used for low-frequency intermittent transfers)

### 5. Slat Conveyor
Unit + In-/On-Floor + No Accumulate
Uses discretely spaced slats connected to a chain
Unit being transported retains its position (like a belt conveyor)
Orientation and placement of the load is controlled
Used for heavy loads or loads that might damage a belt
Bottling and canning plants use flat chain or slat conveyors because of wet conditions, temperature, and cleanliness requirements
Tilt slat conveyor used for sortation
### 6. Flat Belt Conveyor
Unit + On-Floor + No Accumulate
For transporting light- and medium-weight loads between operations, departments, levels, and buildings
When an incline or decline is required
Provides considerable control over the orientation and placement of the load.
No smooth accumulation, merging, and sorting on the belt
The belt is roller or slider bed supported; the slider bed is used for small and irregularly shaped items
In 1957, B.F. Goodrich, Co. patented the Möbius strip for conveying hot or abrasive substances in order to have "both" sides wear equally [14]
### 7. Magnetic Belt Conveyor
Bulk + On-Floor
A steel belt and either a magnetic slider bed or a magnetic pulley is used
To transport ferrous materials vertically, upside down, and around corners

### 8. Troughed Belt Conveyor
Bulk + On-Floor
Used to transport bulk materials
When loaded, the belt conforms to the shape of the troughed rollers and idlers

### 9. Bucket Conveyor
Bulk + On-Floor
Used to move bulk materials in a vertical or inclined path
Buckets are attached to a cable, chain, or belt
Buckets are automatically unloaded at the end of the conveyor run

### 10. Vibrating Conveyor
Bulk + On-Floor
Consists of a trough, bed, or tube
Vibrates at a relatively high frequency and small amplitude in order to convey individual units of products or bulk material
Can be used to convey almost all granular, free-flowing materials
An Oscillating Conveyor is similar in construction, but vibrates at a lower frequency and larger amplitude (not as gentle) in order to convey larger objects such as hot castings
### 11. Screw Conveyor
Bulk + On-Floor
Consists of a tube or U-shaped stationary trough through which a shaft-mounted helix revolves to push loose material forward in a horizontal or inclined direction
One of the most widely used conveyors in the processing industry
Many applications in agricultural and chemical processing
Water screw developed circa 250 BC by Archimedes
### 12. Pneumatic Conveyor
Bulk/Unit + Overhead
Can be used for both bulk and unit movement of materials
Air pressure is used to convey materials through a system of vertical and horizontal tubes
Major advantages are that material is completely enclosed and it is easy to implement turns and vertical moves
#### 12(a) Dilute-Phase Pneumatic Conveyor
Moves a mixture of air and solid
Push (positive pressure) systems push material from one entry point to several discharge points
Pull (negative pressure or vacuum) systems move material from several entry points to one discharge point
Push-pull systems are combinations with multiple entry and discharge points
#### 12(b) Carrier-System Pneumatic Conveyor
Carriers are used to transport items or paperwork (e.g., money from drive-in stalls at banks)
### 13. Vertical Conveyor
Unit + On-Floor + No Accumulate
Used for low-frequency intermittent vertical transfers (cf. vertical chain conveyor can be used for continuous high-frequency vertical transfers
#### 13(a) Vertical Lift Conveyor
Carrier used to raise or lower a load to different levels of a facility (e.g., different floors and/or mezzanines)
Differs from a freight elevator in that it is not designed or certified to carry people
Can be manually or automatically loaded and/or controlled and can interface with horizontal conveyors
#### 13(b) Reciprocating Vertical Conveyor
Utilizes gravity-actuated carrier to lowering loads, where the load overcomes the magnitude of a counterweight
Can only be used to lower a load
Alternative to a chute conveyor for vertical "drops" when load is fragile and/or space is limited
Can be manually or automatically loaded and/or controlled and can interface with horizontal conveyors

### 14. Cart-On-Track Conveyor
Unit + In-Floor + Accumulate
Used to transport carts along a track
Carts are transported by a rotating tube
Connected to each cart is a drive wheel that rests on the tube and that is used to vary the speed of the cart (by varying the angle of contact between the drive wheel and the tube)
Carts are independently controlled
Accumulation can be achieved by maintaining the drive wheel parallel to the tube
### 15. Tow Conveyor
Unit + In-Floor + Accumulate
Uses towline to provide power to wheeled carriers such as trucks, dollies, or carts that move along the floor
Used for fixed-path travel of carriers (each of which has variable path capabilities when disengaged from the towline)
Towline can be located either overhead, flush with the floor, or in the floor
Selector-pin or pusher-dog arrangements can be used to allow automatic switching (power or spur lines)
Generally used when long distance and high frequency moves are required
### 16. Trolley Conveyor
Unit + Overhead + No Accumulate
Uses a series of trolleys supported from or within an overhead track
Trolleys are equally spaced in a closed loop path and are suspended from a chain
Carriers are used to carry multiple units of product
Does not provide for accumulation
Commonly used in processing, assembly, packaging, and storage operations
### 17. Power-and-Free Conveyor
Unit + Overhead/On-Floor + Accumulate
Similar to trolley conveyor due to use of discretely spaced carriers transported by an overhead chain; however, the power-and-free conveyor uses two tracks: one powered and the other nonpowered (or free)
Carriers can be disengaged from the power chain and accumulated or switched onto spurs
Termed an Inverted Power-and-Free Conveyor when tracks are located on the floor
### 18. Monorail
Unit + Overhead + Accumulate
Overhead single track (i.e., mono-rail) or track network on which one or more carriers ride
Carriers: powered (electrically or pneumatically) or nonpowered
Carrier can range from a simple hook to a hoist to an intelligent-vehicle-like device
Single-carrier, single-track monorail similar to bridge or gantry crane
Multi-carrier, track network monorail similar to both a trolley conveyor, except that the carriers operate independently and the track need not be in a closed loop, and a fixed-path automatic guided vehicle (AGV) system, except that it operates overhead
Termed an Automated Electrified Monorail (AEM) system when it has similar control characteristics as an AGV system
### 19. Sortation Conveyor
Unit + On-Floor/Overhead
Sortation conveyors are used for merging, identifying, inducting, and separating products to be conveyed to specific destinations
#### 19(a) Sortation Conveyor: Diverter

Stationary or movable arms that deflect, push, or pull a product to desired destination
Since they do not come in contact with the conveyor, they can be used with almost any flat surface conveyor
Usually hydraulically or pneumatically operated, but also can be motor driven
Simple and low cost
#### 19(b) Sortation Conveyor: Pop-Up Device

One or more rows of powered rollers or wheels or chains that pop up above surface of conveyor to lift product and guide it off conveyor at an angle; wheels are lowered when products not required to be diverted
Only capable of sorting flat-bottomed items
Pop-up rollers are generally faster than pop-up wheels
#### 19(c) Sortation Conveyor: Sliding Shoe Sorter
Sliding shoe sorter (a.k.a. moving slat sorter) uses series of diverter slats that slide across the horizontal surface to engage product and guide it off conveyor
Slats move from side to side as product flows in order to divert the product to either side
Gentle and gradual handling of products
#### 19(d) Sortation Conveyor: Tilting Device
Trays or slats provide combined sorting mechanism and product transporter
Can accommodate elevation changes
Tilt tray sorters usually designed in continuous loops with a compact layout and recirculation of products not sorted the first time
Tilt slat sorters carry products on flat-surface slat conveyor and can handle wider variety of products compared to tilt tray
#### 19(e) Sortation Conveyor: Cross-Belt Transfer Device
Either continuous loop, where individual carriages are linked together to form an endless loop, or train style (asynchronous), where a small number of carriers tied together with potential for several trains running track simultaneously
Each carriage equipped with small belt conveyor, called the cell, that is mounted perpendicular to direction of travel of loop and discharges product at appropriate destination
Automatically separates single line of products into multiple in-line discharge lines

## I-B. Cranes
Cranes are used to move materials over variable paths within a restricted area. The major types of cranes are:
Jib crane / Bridge crane / Gantry crane / Stacker crane

General characteristics of cranes:
- Used to move loads over variable (horizontal and vertical) paths within a restricted area
- Used when there is insufficient (or intermittent) flow volume such that the use of a conveyor cannot be justified
- Provide more flexibility in movement than conveyors
- Provide less flexibility in movement than industrial trucks
- Loads handled are more varied with respect to their shape and weight than those handled by a conveyor
- Most cranes utilize hoists for vertical movement, although manipulators can be used if precise positioning of the load is required
### 1. Jib Crane
Operates like an arm in a work area, where it can function as a manipulator for positioning tasks
A hoist is attached to the arm for lifting
Arm mounted on the wall or attached to a floor mounted support
Arm can rotate 360°
The hoist can move along the arm
### 2. Bridge Crane
Bridge mounted on tracks that are located on opposite walls of the facility
Enables three-dimensional handling
Top riding (heavier loads) or underhung (more versatile) versions of the crane
Underhung crane can transfer loads and interface with other MHS (e.g., monorail systems)

### 3. Gantry Crane

Single leg, double leg, and mobile types of gantry cranes
Similar to a bridge crane except that it is floor supported at one or both ends instead of overhead (wall) supported
Used to span a smaller portion of the work area as compared to a bridge crane
The supports can be fixed in position or they can travel on runways
Can be used outdoors when "floor" supported at both ends
### 4. Stacker Crane
Similar to a bridge crane except that, instead of a hoist, it uses a mast with forks or a platform to handle unit loads
Considered "fork trucks on a rail"
Used for storing and retrieving unit loads in storage racks, especially in high-rise applications in which the racks are more than 50 feet high
Can be controlled remotely or by an operator in a cab on the mast Can be rack supported
## I-C. Industrial Trucks
Industrial trucks are used to move materials over variable paths, with no restrictions on the area covered by the movement. The major types of industrial trucks are:
Hand truck / Two-wheeled hand truck / Dolly / Floor hand truck / Pallet jack / Manual pallet jack / Powered pallet jack / Walkie stacker / Manual walkie stacker / Powered walkie stacker / Pallet truck / Platform truck / Walkie platform truck / Rider platform truck / Counterbalanced lift truck / Sit-down counterbalanced lift truck / Stand-up counterbalanced lift truck	Narrow-aisle straddle truck / Narrow-aisle reach truck / Turret truck / Operator-down turret truck / Operator-up turret truck / Order picker / Sideloader / Tractor-trailer / Personnel and burden carrier / Automatic guided vehicle (AGV) / Tow AGV / Unit load AGV / Assembly AGV / Light load AGV / Fork AGV

Industrial trucks:
- Used to move materials over variable (horizontal) paths with no restrictions on the area covered (i.e., unrestricted area)
- Provide vertical movement if the truck has lifting capabilities
- Used when there is insufficient (or intermittent) flow volume such that the use of a conveyor cannot be justified
- Provide more flexibility in movement than conveyors and cranes
- Not licensed to travel on public roads—"commercial trucks" are licensed to travel on public roads
Characteristics:
Pallet/Non-Pallet: Does the truck have forks for handling pallets, or does the truck have a flat surface on which to place loads. Non-Pallet => (usually) other means required to load truck.
Manual/Powered: Does the truck have manual or powered vertical (lifting) and/or horizontal (travel) movement capabilities. Manual => walk => operator provides the force needed for lifting loads and/or pushing the vehicle. Powered => on-board power source (e.g., batteries) used for lifting and/or travel.
Walk/Ride: For non-automated trucks, can the operator ride on the truck (in either a standing or sitting position) or is the operator required to walk with the truck during travel. Walk => manual or powered travel possible => powered travel speed limited to a normal walking pace. Ride => powered => travel speed can be faster than a walking pace.
Stack/No Stack: Can the truck be used to lift loads for stacking purposes. Stack => can also be used as no stack => more expensive to add stacking capability. No Stack may lift a load a few inches to clear the floor for subsequent travel (e.g., pallet jack), but the loads cannot be stacked on top of each other or on shelves.
Narrow Aisle: Is the lift truck designed to have a small turning radius or does it not have to turn at all in an aisle when loading/unloading. Narrow Aisle => greater cost and (usually) standing operator => less aisle space required. Counterbalance and/or straddle used for load support. Small turning radius => load support via straddle or reaching capabilities. No turning required => even narrower aisle => only one-side loading (sideloaders) or the capability to rotate the load (turret truck).
Automated: Is the truck automated so that it can transport loads without requiring an operator. Non-Automated => direct labor cost of operator is by far the largest cost to operate a non-automated truck. Semi-Automated => operator used to control loading/unloading, but automated transport control (e.g., the S/R machine of a Man-on-board AS/RS). Automated => Automated Guided Vehicle (AGV) => no direct labor cost, but higher equipment costs.
### 1. Hand Truck
Non-pallet + manual + no stack
#### 1(a) Two-Wheeled Hand Truck
Load tilted during travel
#### 1(b) Dolly
Three or more wheeled hand truck with a flat platform in which, since it has no handles, the load is used for pushing
#### 1(c) Floor Hand Truck
Four or more wheeled hand truck with handles for pushing or hitches for pulling
Sometimes referred to as a "cart" or "(manual) platform truck"
### 2. Pallet Jack
Pallet + walk + no stack
Front wheels are mounted inside the end of the forks and extend to the floor as the pallet is only lifted enough to clear the floor for subsequent travel
Pallet restrictions: reversible pallets cannot be used, double-faced nonreversible pallets cannot have deckboards where the front wheels extend to the floor, and enables only two-way entry into a four-way notched-stringer pallet because the forks cannot be inserted into the notches
#### 2(a) Manual Pallet Jack
Pallet + walk + no stack + manual
Manual lifting and/or travel
#### 2(b) Powered Pallet Jack
Pallet + walk + no stack + powered
Powered lifting and/or travel

### 3. Walkie Stacker
Pallet + walk + stack
#### 3(a) Manual Walkie Stacker
Pallet + walk + stack + manual
Manual lifting and/or travel (and straddle load support)
#### 3(b) Powered Walkie Stacker
Pallet + walk + stack + powered
Powered lifting and/or travel (and either counterbalance or straddle load support)

### 4. Pallet Truck
Pallet + ride + no stack
Same pallet restrictions as a pallet jack
Control handle typically tilts to allow operator to walk during loading/unloading
Powered pallet jack is sometimes referred to as a "(walkie) pallet truck"

### 5. Platform Truck
Non-pallet + powered + no stack
Platform used to provide support for nonpalletized loads
Used for skid handling; platform can lift skid several inches to allow it to clear the floor
Greater lifting capacity compared to fork trucks because the platform provides a greater lifting surface to support a load
#### 5(a) Walkie Platform Truck
Non-pallet + powered + no stack + walk
Operator walks next to truck
Floor hand truck is sometimes referred to as a "(manual) platform truck"
#### 5(b) Rider Platform Truck
Non-pallet + powered + no stack + ride
Operator can ride on truck

### 6. Counterbalanced (CB) Lift Truck
Pallet + ride + stack
Also referred to as fork truck.
Weight of vehicle (and operator) behind the front wheels of truck counterbalances weight of the load (and weight of vehicle beyond front wheels); front wheels act as fulcrum or pivot point.
Rated capacity reduced for load centers greater than 24 in. and lift heights greater than 13 ft.
Workhorses of material handling because of their flexibility: indoor/outdoor operation over a variety of different surfaces; variety of load capacities available; and variety of attachments available—fork attachments can replace the forks (e.g., carton clamps) or enhance the capabilities of the forks (e.g., blades for slipsheets).
#### 6(a) Sit-Down Counterbalanced Lift Truck
Operator sits down
12-13 ft. minimum aisle width requirement
#### 6(b) Stand-Up Counterbalanced Lift Truck
Operator stands up, giving vehicle narrow-aisle capability
9-11 ft. minimum aisle width requirement
Faster loading/unloading time compared to NA straddle and reach trucks

### 7. Narrow-Aisle (NA) Straddle Truck
Similar to stand-up CB lift truck, except outrigger arms straddle a load and are used to support the load instead of the counterbalance of the truck
7-8 ft. minimum aisle width requirement
Less expensive than stand-up CB lift truck and NA reach truck
Since the load is straddled during stacking, clearance between loads must be provided for the outrigger arms
Arm clearance typically provided through the use of load-on-beam rack storage or single-wing pallets for load-on-floor storage
### 8. Narrow-Aisle (NA) Reach Truck
Similar to both stand-up CB lift truck and NA straddle truck
8-10 ft. minimum aisle width requirement
Load rests on the outrigger arms during transport, but a pantograph (scissors) mechanism is used for reaching, thereby eliminating the need to straddle the load during stacking
Reaching capability enables the use of shorter outrigger arms (arms > 1/2 load depth) as compared to NA straddle truck (arms = load depth)
Counterbalance of the truck used to support the load when it extends beyond the outrigger arms
Although the NA reach truck requires slightly wider aisles than a NA straddle truck since its outrigger arms do not enter a rack during storage, it does not require arm clearance between loads (arm clearance is still required when the truck must enter a storage lane when block stacking or drive-in or -through racks are used)
Extended reaching mechanisms are available to enable double-deep storage

### 9. Turret Truck
Greater stacking height compared to other narrow-aisle trucks (40 ft. vs. 25 ft.), but greater investment cost
Forks rotate to allow for side loading and, since truck itself does not rotate during stacking, the body of the truck can be longer to increase its counterbalance capability and to allow the operator to sit
Can function like a sideloader for transporting greater-than-pallet-size load
#### 9(a) Operator-Down Turret Truck
Operator not lifted with the load
5-6 ft. minimum aisle width requirement
Termed a swingmast truck (picture shown) when, instead of just the forks, the entire mast rotates (thus can store on only one side of a aisle while in aisle)
#### 9(b) Operator-Up Turret Truck
Operator lifted with the load to allow precise stacking and picking
5-7 ft. minimum aisle width requirement

### 10. Order Picker
Similar to NA straddle truck, except operator lifted with the load to allow for less-than-unit-load picking
Typically has forks to allow the truck to be used for pallet stacking and to support a pallet during less-than-pallet-load picking
"Belly switch" used for operator safety during picking

### 11. Sideloader
Forks mounted perpendicular to direction of travel to allow for side loading and straddle load support
5-6 ft. minimum aisle width requirement
Can be used to handle greater-than-pallet-size loads (e.g., bar stock)

### 12. Tractor-Trailer
Non-load-carrying tractor used to pull a train of trailers (i.e., dollies or floor hand trucks)
Extends the transporting capacity of floor hand trucks
Typically used at airports for baggage handling

### 13. Personnel and Burden Carrier
Non-load-carrying vehicle used to transport personnel within a facility (e.g., golf cart, bicycle, etc.)
### 14. Automatic Guided Vehicle (AGV)
AGVs do not require an operator
Good for high labor cost, hazardous, or environmentally sensitive conditions (e.g., clean-room)
Also termed "automated" guided vehicle
AGVs good for low-to-medium volume medium-to-long distance random material flow operations (e.g., transport between work cells in a flexible manufacturing system (FMS) environment)
Two means of guidance can be used for AGV systems:
Fixed path: Physical guidepath (e.g., wire, tape, paint) on the floor used for guidance
Free-ranging: No physical guidepath, thus easier to change vehicle path (in software), but absolute position estimates (from, e.g., lasers) are needed to correct dead-reckoning error
#### 14(a) Tow AGV
Used to pull a train of trailers
Automated version of a tractor trailer
Trailers usually loaded manually (early type of AGV, not much used today)
#### 14(b) Unit Load AGV
Have decks that can be loaded manually or automatically
Deck can include conveyor or lift/lower mechanism for automatic loading
Typically 4 by 4 feet and can carry 1–2,000 lb. loads
Typically less than 10 vehicles in AGV system
#### 14(c) Assembly AGV
Used as assembly platforms (e.g., car chassis, engines, appliances)
Greatest development activity during the 1980s (alternative to AEMs)
Typically 50–100 vehicles in AGV system
#### 14(d) Light Load AGV
Used for small loads (< 500 lbs), e.g., components, tools
Typically used in electronics assembly and office environments (as mail and snack carriers)
#### 14(e) Fork AGV
Counterbalanced, narrow-aisle straddle, and sideloading versions available
Typically have sensors on forks (e.g., infrared sensors) for pallet interfacing
## I-D. No equipmentConveyors
Material can be transported manually using no equipment.
Under ideal circumstances, maximum recommended weight for manual lifting to avoid back injuries is 51 lbs.
Recommendation based on NIOSH (National Institute for Occupational Safety and Health) 1994 Lifting Equation, which uses six multipliers to reduce maximum recommended weight for less than ideal lifting tasks.

## II. Positioning Equipment
Positioning equipment is used to handle material at a single location so that the material is in the correct position for subsequent handling, machining, transport, or storage. Unlike transport equipment, positioning equipment is usually used for handling at a single workplace. Material can also be positioned manually using no equipment. The major types of positioning equipment are:
Manual (no equipment) / Lift/tilt/turn table / Dock leveler / Ball transfer table / Rotary index table / Parts feeder / Air film device	Hoist / Balancer / Manipulator / Rigid-link manipulator / Articulated jib crane manipulator / Vacuum manipulator / Industrial robot

As compared to manual handling, the use of positioning equipment can provide the following benefits [Modern Materials Handling, Sept. 1993]:
- raise the productivity of each worker when the frequency of handling is high,
- improve product quality and limit damage to materials and equipment when the item handled is heavy or awkward to hold and damage is likely through human error or inattention, and
- reduce fatigue and injuries when the environment is hazardous or inaccessible.
### 1. Manual (No Equipment)
Material can be positioned manually using no equipment
Under ideal circumstances, maximum recommended weight for manual lifting to avoid back injuries is 51 lbs.
Recommendation based on NIOSH (National Institute for Occupational Safety and Health) 1994 Lifting Equation, which uses six multipliers to reduce maximum recommended weight for less than ideal lifting tasks
### 2. Lift/Tilt/Turn Table
Used when positioning involves the lifting, tilting, or turning of a load
Can be used to reduce or limit a worker’s lifting and/or reaching motions
Pallet load levelers are lift and turn tables used in manual palletizing to reduce the amount of bending and stooping involved with manually loading a pallet by combining a lifting and turning mechanism with a device that lowers the table as each layer is completed so that loading always takes place at the optimal height of 30 inches
### 3. Dock Leveler
Used at loading docks to compensate for height differences between a truck bed and the dock
### 4. Ball Transfer Table
Used in conveyor systems to permit manual transfer to and from machines and conveyors and between different sections of conveyors
Since loads are pushed on the table, ball friction limits the maximum load weight to 600 lbs.

### 5. Rotary Index Table
Used for the synchronous transfer of small parts from station to station in a single workcenter
Circular table rotates in discrete intermittent steps to advance parts between stations located along its perimeter
Since each part moves between stations at the same time, it is difficult to put buffers between stations
Different from conveyors used as in-line indexing machines, where linear transfers can take place between multiple workcenters separated by long distances, since a rotary index table is restricted to circular transfers with a single compact workcenter

### 6. Parts Feeder
Used for feeding and orienting small identical parts, particularly in automatic assembly operations [13]
Motion of parts in a random pile channeled so that each part automatically assumes a specified orientation, where the symmetries of a part define its possible orientations
Motion can be imparted through vibration, gravity, centrifugal force, tumbling, or air pressure
In a vibratory bowl feeder, the most versatile type of parts feeder, parts are dumped into a bowl and then move vibrate uphill along a track towards an outlet, where rejected parts fall off the track and are recycled
Parts feeders can be used to provide inspection capabilities with respect to the shape and weight of parts (e.g., the coin feeder of a vending machine)

### 7. Air Film Device
Used to enable precision positioning of heavy loads
Sometimes referred to as "air pallets"
Can be used in place of cranes and hoists
Thin film of compressed (10–50 psi) air used to float loads of up to 300,000 lbs. so that a horizontal push of 1 lb. can move 1000 lb. load; floating action enables load to rotated or translated in any direction in the horizontal plane
Requires a smooth floor surface against which air streams underneath the device can push
Can be used in warehousing as the mechanism to convert stationary racks into sliding racks

### 8. Hoist
Used for vertical translation (i.e., lifting and lowering) of loads
Frequently attached to cranes and monorails to provide vertical translation capability
Can be operated manually, electrically, or pneumatically

### 9. Balancer
Mechanism used to support and control loads so that an operator need only guide a balanced ("weightless") load, thus providing precision positioning
Can also be attached to hoists and manipulators

### 10. Manipulator
Used for vertical and horizontal translation and rotation of loads
Acting as "muscle multipliers," manipulators counterbalance the weight of a load so that an operator lifts a small portion (1%) of the load’s weight
Can be powered manually, electrically, or pneumatically
Manipulator’s end-effector can be equipped with mechanical grippers, vacuum grippers, electromechanical grippers, or other tooling
Manipulators fill the gap between hoists and industrial robots: they can be used for a wider range of positioning tasks than hoists and are more flexible than industrial robots due to their use of manual control
#### 10(a) Rigid-Link Manipulator
Although similar in construction, a rigid-link manipulator is distinguished from an industrial robot by the use of an operator for control as opposed to automatic computer control
#### 10(b) Articulated Jib Crane Manipulator
Extends a jib crane’s reaching capability in a work area through the use of additional links or "arms"
#### 10(c) Vacuum Manipulator
Provides increased flexibility because rigid links are not used (vacuum, rigid-link, and articulated jib crane manipulators can all use vacuum gripper end-effectors)

### 11. Industrial Robot
Used in positioning to provide variable programmed motions of loads
"Intelligent" industrial robots utilize sensory information for complex control actions, as opposed to simple repetitive "pick-and-place" motions
Industrial robots also used for parts fabrication, inspection, and assembly tasks
Consists of a chain of several rigid links connected in series by revolute or prismatic joints with one end of the chain attached to a supporting base and the other end free and equipped with an end-effector
Robot’s end-effector can be equipped with mechanical grippers, vacuum grippers, electromechanical grippers, welding heads, paint spray heads, or any other tooling
Although similar in construction, an industrial robot is distinguished from a manipulator by the use of programmed control logic as opposed manual control
Pick-and-place industrial robots used as automatic palletizers
Mobile robots similar in construction to free-ranging AGVs
Can be powered manually, electrically, or pneumatically

## III. Unit Load Formation Equipment
Unit load formation equipment used to restrict materials so that they maintain their integrity when handled a single load during transport and for storage. The major types of unit load formation equipment are ([+] = more info):
Self-restraining (no equipment) / Pallets / Skids / Slipsheets [+] / Tote pans / Pallet boxes/skid boxes / Bins/baskets/racks / Cartons / Bags	Bulk load containers / Crates / Intermodal containers / Strapping/tape/glue / Shrink-wrap/stretch-wrap / Palletizers / Manual palletizing / Robotic pick and place palletizers / Conventional stripper plate palletizers

Advantages of unit loads:
- More items can be handled at the same time, thereby reducing the number of trips required and, potentially, reducing handling costs, loading and unloading times, and product damage.
- Enables the use of standardized material handling equipment.
Disadvantages of unit loads:
- Time spent forming and breaking down the unit load.
- Cost of containers/pallets and other load restraining materials used in the unit load
- Empty containers/pallets may need to be returned to their point of origin.

### 1. Self-Restraining (No Equipment)
One or more items that can maintain their integrity when handled as a single item (e.g., a single part or interlocking parts)

### 2. Pallets
Platform with enough clearance beneath its top surface (or face) to enable the insertion of forks for subsequent lifting purposes
Materials: Wood (most common), paper, plastic, rubber, and metal
Size of pallet is specified by its depth (i.e., length of its stringers or stringer boards) and its width (i.e., length its deckboards)—pallet height (typically 5 in.) is usually not specified; orientation of stringers relative to deckboards of pallet is specified by always listing its depth first and width last: Depth (stringer length) x Width (deckboard length)
48 x 40 in. pallet is most popular in US (27% of all pallets—no other size over 5%) because its compatibility with railcar and truck trailer dimensions
1200 x 800 mm "Euro-Pallet" is the standard pallet in Europe

### 3. Skids
Platform (typically metal) with enough clearance beneath its top surface to enable a platform truck to move underneath for subsequent lifting purposes
Forks can also be used to handle skids since the clearance of a skid is greater than that of a pallet
Compared to a pallet, a skid is usually used for heavier loads and when stacking is not required; a metal skid can lift heavier loads than an equal-weight metal pallet because it enables a platform truck to be used for the lifting, with the platform providing a greater lifting surface to support the skid as compared to the forks used to support the pallet

### 4. Slipsheets
Thick piece of paper, corrugated fiber, or plastic upon which a load is placed
Handling method: tabs on the sheet are grabbed by a special push/pull lift truck attachment
Advantages: usually used in place of a pallet for long-distance shipping because their cost is 10–30% of pallet costs and their weight and volume is 1–5% of a pallet
Disadvantages: slower handling as compared to pallets; greater load damage within the facility; special lift truck attachment reduces the vehicle’s load capacity

### 5. Tote Pans
Reusable container used to unitize and protect loose discrete items
Typically used for in-process handling
Returnable totes provide alternative to cartons for distribution

### 6. Pallet Boxes/Skid Boxes
Reusable container used to unitize and protect loose items for fork/platform truck handling

### 7. Bins/Baskets/Racks
Storage equipment that also can be used to unitize and protect loose discrete items

### 8. Cartons
Disposable container used to unitize and protect loose discrete items
Typically used for distribution
Dimensions always specified as sequence: Length x Width x Depth, where length is the larger, and width is the smaller, of the two dimension of the open face of the carton, and depth is the distance perpendicular to the length and width
Large quantities of finished carton blanks or knocked-down cartons can be stored on pallets until needed

### 9. Bags
Disposable container used to unitize and protect bulk materials
Typically used for distribution
Polymerized plastic ("poly") bags available from light weight (1 mil.) to heavy weight (6 mil.) in flat and gusseted styles
Dimensions of bag specified as: Width x Length, for flat bags, and Width x Depth (half gusset) x Length, for gusseted bags

### 10. Bulk Load Containers
Reusable container used to unitize and protect bulk materials
Includes drums, cylinders, etc.
Used for both distribution and in-process handling

### 11. Crates
Disposable container used to protect discrete items
Typically used for distribution

### 12. Intermodal Containers
Reusable container used to unitize and protect loose discrete items
Enables a load to be handled as a single unit when it is transferred between road, rail, and sea modes of transport; e.g., the container can be unloaded from a cargo ship and loaded onto a truck as a single unit
It is not as common to use intermodal containers for airfreight transport because of aircraft shape and weight restrictions
The standard outside dimensions of intermodal containers are: 20 or 40 ft. in length; 8 ft. in width; and 8, 8.5, or 9.5 ft. in height; less 8 in. of length, 5 in. of width, and 9.5 in. of height to determine the inside dimensions. Typical sea transport costs per 40-ft container are: $3000–4000 from Japan to the US west coast, $4000–5000 from Singapore to the US west coast, and $2500–3500 from Europe to the US east coast; transport costs for a 20-ft. container is 70% of the costs of a 40-ft. container [15]

### 13. Strapping/Tape/Glue
Used for load stabilization
Straps are either steel or plastic
Plastic strapping that shrinks is used to keep loads from becoming loose during shipment

### 14. Shrink-Wrap/Stretch-Wrap
Used for load stabilization
In shrink-wrapping, a film or bag is placed over the load and then heat is applied to shrink the film or bag; allows irregular loads to be stabilized; manual or automatic; most shrink-wrap applications are being replaced by stretch-wrapping
In stretch-wrapping, a film is wound around the load while the film is stretched; allows irregular loads to be stabilized; manual or automatic; as compared to shrink-wrapping, stretch-wrapping has lower material, labor, and energy costs

### 15. Palletizers
Used for load formation.
Three general methods of building (or "palletizing") unit loads:
#### 15(a) Manual Palletizing
Operators arrange items into the desired pattern used to form the unit load
Since the ergonomics of loading and unloading are important (e.g., vertically, the prime working zone is between the knees and the chest; horizontally, reaches of more than 24 in. with a load should be avoided), lift and turn tables are often used
Semi-mechanized palletizers use operators to arrange items into the desired pattern for each layer of the unit load and a powered device is used to transfer layers onto a pallet and then lower the load for the next layer
#### 15(b) Robotic Pick and Place Palletizers
Fully automated device to build unit loads
Used when flexibility is required (e.g., the "Distributor’s Pallet Loading Problem")
Greatest limitation is capacity, typically 6 cycles per minute; capacity is determined by the number of items handled with each pick operation
Operators arrange items into the desired pattern for each layer of the unit load and a powered device is used to transfer layers onto a pallet and then lower the load for the next layer
#### 15(c) Conventional Stripper Plate Palletizers

Fully automated device to build unit loads
Used when high throughput of identical loads is required (e.g., the "Manufacturer’s Pallet Loading Problem")
Capacity is typically greater (30–180 items per minute) than pick and place because an entire layer is placed on the load at one time; not as flexible as pick and place
Preformed layer of items (cases) are indexed onto the stripper plate (or apron); when properly positioned over the pallet, the apron is pulled out from underneath the layer to deposit the layer onto the pallet
"In-line" pattern formation (top picture)—flexible patterns are not possible; ideal for high speed operation (up to 180 items per minute); takes up more room (larger machine) than right angle
"Right angle" pattern formation (bottom picture)—very flexible patterns are possible; can handle a wide variety of case sizes and types; limited capacity (up to 80 items per minute); compact design

## IV. Storage Equipment
Storage equipment used for holding or buffering materials over a period of time. The major types of storage equipment are:
Block stacking (no equipment) / Selective pallet rack / Drive-through rack / Drive-in rack / Flow-through rack / Push-back rack / Sliding rack / Cantilever rack / Stacking frame	Shelves/bins/drawers / Storage carousel / Automatic storage/retrieval systems (AS/RS) / Unit load AS/RS / Miniload AS/RS / Man-on-board AS/RS / Deep-lane AS/RS / Split case order picking system / Mezzanine

The most common reason for storing a product allows the other elements of production to operate more efficiently on a per-unit basis because the fixed costs associated with utilizing the element can be spread over more products; e.g., storing up to a truckload of product in a facility reduces the per-unit costs of shipping; and buffering or storage of WIP enables batch production which reduces the per-unit setup costs.
Other potential reasons for storage include: time bridging—allows product to be available when it is needed (e.g., storing spare machine parts at the facility); processing—for some products (e.g., wine), storage can be considered as a processing operation because the product undergoes a required change during storage; and securing—e.g., nuclear waste storage.

### 1. Block Stacking (No Equipment)
Bulk storage using block stacking can result in the minimum cost of storage since cube utilization is high and no storage medium is required, but material accessibility is low since only the top of the front stack is accessible and loads at bottom of a stack must not require support
Storage racks are used when support and/or material accessibility is required

### 2. Selective Pallet Rack
Most popular type of storage rack
Pallets are supported between load-supporting beams
Special attachments and decking can be used to make the racks capable of supporting other types of unit loads besides pallets (e.g., coils, drums, skids)
Selective racks can be used for the following types of storage:
Standard—single-deep storage using a counterbalanced lift truck
Narrow-Aisle—storage using a narrow-aisle lift truck
Deep-Reach—greater than single-deep storage (typically double-deep storage)

### 3. Drive-Through Rack
Loads are supported by rails attached to the upright beams
Lift trucks are driven between the uprights beams
Requires similar-width loads
Open at both ends, allowing access from both ends (FIFO)

### 4. Drive-In Rack
Same as drive-through rack, except closed at one end, allowing entry from only one end (LIFO)
### 5. Flow-Through Rack
Loads are supported on an incline to enable gravity-based movement of the loads within the rack (via, e.g., a gravity roller conveyor)
Loaded at the higher end and unloaded at the lower end (FIFO)

### 6. Push-Back Rack
Same as push-back rack, except loaded and unloaded at the lower end and closed at the higher end (LIFO)

### 7. Sliding Rack
Only one mobile aisle is used to access several rows of racks
Location of the aisle is changed by sliding the rows of racks along guide rails in the floor
Typically found in library stacks

### 8. Cantilever Rack
Loads are supported by cantilever "arms"
Used to store long loads (e.g., bar stock, pipes, lumber)
Similar to pallet racks, except the front upright beams and the front supporting beams are eliminated

### 9. Stacking Frame
Interlocking units that enable stacking of a load so that crushing does not occur
Can be disassembled and stored compactly when not in used
Pallet frames can be used to enable multilevel block stacking

### 10. Shelves/Bins/Drawers

### 11. Storage Carousel
Carousel consists of a set of vertically or horizontally revolving storage baskets or bins
Materials (and the storage medium) move to the operator, "part-to-man," for end-of-aisle picking
Each level of the carousel can rotate independently in a clockwise or counter-clockwise direction
Control ranges from manually activated push buttons to automated computer controlled systems
Provides an alternative to typical "man-to-part" AS/RS, where the S/R machine moves to the part
Similar to a trolley conveyor with storage baskets
### 12. Automatic Storage/Retrieval Systems (AS/RS)
Consists of an integrated computer-controlled system that combines the storage medium, transport mechanism, and controls with various levels of automation for fast and accurate random storage of products and materials
Storage/retrieval (S/R) machine in an AS/RS operates in narrow aisle, serving rack slots on both sides of aisle; can travel in horizontal (along the aisle) and vertical (up and down a rack) directions at same time
Advantages: fewer material handlers, better material control (including security), and more efficient use of storage space
Disadvantages: high capital and maintenance costs, and difficult to modify
#### 12(a) Unit Load AS/RS
Used to store/retrieve loads that are palletized or unitized and weigh over 500 lbs.
Stacking heights up to 130 ft. high, with most ranging from 60 to 85 ft. high; 5 to 6 ft. wide aisles; single- or double-deep storage racks
#### 12(b) Miniload AS/RS
Used to store/retrieve small parts and tools that can be stored in a storage bin or drawer
End-of-aisle order picking and replenishment
Stacking heights range from 12 to 20 ft.; bin capacities range from 200 to 750 lbs.
Termed a "microload AS/RS" when used in assembly, kitting, and testing operations to deliver small containers of parts to individual workstations, where workstations are typically located on the sides of a pair of racks and the S/R machine operates between the racks to move containers to openings in the racks (storage lanes) located next to each station
#### 12(c) Man-On-Board AS/RS
Used for in-aisle picking; operator picks from shelves, bins, or drawers within the storage structure
Manual or automatic control
S/R machine is similar to an order picker or turret truck and can sometimes operate as an industrial truck when outside an aisle, except the S/R is guided along a rail when operating in an aisle
#### 12(d) Deep-Lane AS/RS
Similar to unit load AS/RS, except loads can be stored to greater depths in the storage rack
A rack-entry vehicle is used to carry loads into the racks from the S/R machine, and is controlled by the S/R machine
Termed an "automated item retrieval system" when used to automatically retrieve individual items or cases, with replenishment (storage) taking place manually from the rear of a flow-through storage lane and items are pushed forward with a rear-mounted pusher bar for automatic picking from the front of the storage lane

### 13. Split-Case Order Picking System
Unlike an AS/RS, a split-case order picking system enables fully automated picking of individual items
Two general categories of split-case order picking system are robotic based systems and magazine/dispenser based systems
Robotic based systems are similar in construction to robotic pick and place palletizers
Magazine/dispenser based systems are similar to vending machines, but larger in scale
"A-Frame" dispenser system (pictured) is popular within pharmaceutical distribution centers; items are dispensed onto a belt conveyor that carries them into a container

### 14. Mezzanine
Inexpensive means of providing additional storage or office space
Makes use of clear space over activities not requiring much headroom (e.g., restrooms, block storage, etc.)
At least 14 ft. of clear space is needed for a mezzanine

## V. Identification and Control Equipment
Identification and control equipment is used to collect and communicate the information that is used to coordinate the flow of materials within a facility and between a facility and its suppliers and customers. The major types of identification and communication equipment are:
Manual (no equipment) / Bar codes / Radio frequency (RF) tag / Magnetic stripe	Machine vision / Portable data terminal / Electronic data interchange (EDI)/Internet

### 1. Manual (No Equipment)
The identification of materials and associated communication can be performed manually with no specialized equipment
Although it is sometimes possible to manually coordinate the operation of a material handling system, it becomes more difficult to due so as the speed, size, and complexity of the system increases
### 2. Bar Codes
Unique bar/space patterns represent various alphanumeric characters
Bar code system consists of bar code label, bar code scanner, and bar code printer
Contact bar code scanners use pen or wand to read labels
Noncontact bar code scanners include fixed beam, moving beam, and omnidirectional
1-D codes are most common; 2-D codes enable much greater data storage capability

### 3. Radio Frequency (RF) Tag
Data encoded on chip encased in a tag
Noncontact: can be read when the tag is within 30 ft. of an antenna
Tags can either be attached to a container, or permanently or temporarily to an item
RF tags have greater data storage capability than bar codes
### 4. Magnetic Stripe
Data encoded on a magnetic stripe that is readable in almost any environment
Requires contact with a reader
Greater storage capability and more expensive than bar codes

### 5. Machine Vision
Does not require explicit encoding of data since objects can be identified by their physical appearance
Noncontact, but typically requires structured lighting
More flexible than other identification equipment, but less robust

### 6. Portable Data Terminal
Handheld, arm-mounted, or vehicle-mounted data storage and communication device
Communicates with a host computer via a radio frequency or infrared link
Variety of input devices available: keyboard, bar code scanner, voice headset
### 7. Electronic Data Interchange (EDI)/Internet
Electronic data interchange (EDI) provides standards for inter-corporate transfer of purchase orders, invoices, shipping notices, and other frequently used business documents
Prior to the Internet, EDI required expensive dedicated value added networks (VANs)
EDI is critical for implementing JIT manufacturing