Physics 4BL, Lab 2
403942345
2012-10-30

Experimental Results:

Ohms Law:

The two resistors r and R were connected in series to the function generator. The ADC was used to sample the voltages across each resistor. Resistor r is used to determine the current to produce the graph in Figure 1.

Figure 1
Ohms law (resistor circuit)
Current vs. Voltage (across R)
Voltage (V)
Current (mA)
Measured Resistances
Resistor	Resistance (Ω)
r	99
R	992
r||R	90

Diode:

In the diode circuit, a resistor and diode were connected in series to the function generator. In Figure 2 it is shown that current increases exponentially with increased voltage.

Figure 2
Diode Circuit
Current vs. Voltage (across diode)
Diode Voltage (V)
Current (A)
Component	Value
diode	10 mH
diode internal resistance	729 Ω
resistor	99

Copper Wire:

In this experiment, the resistance of the copper wire was measured at different temperatures. Also, the mass of the copper roll was measured by weighing, and other properties were given.

Temperature (K)	Resistance (Ω)
293	10.60
77	1.80

Measured	Given
Mass (g)	Diameter (cm)	Density (g/cm3)
241.8	5.33e-2	8.92

Capacitor Transient:

First, the function generator was connected to the oscilloscope so we could manipulate the mean voltage and amplitude until the voltage oscillated between 0 and 4. A capacitor and resistor was connected in series to the function generator, then the voltages were sampled (see Figure 3).

Resistor (Ω)	Capacitor (μF)	Frequency (Hz)	Mean Voltage (V)	Amplitude (V)
9850	1	16.16	1.95	2.0

Figure 3
Capacitor Transient (RC circuit)
Voltage vs. Time
Time (s)
Voltage (V)

Inductor Transient:

In this circuit, two resistors, r1 and r2, were used in addition to the inductor. r2 was connected with L in series, and that series circuit was connected in parallel with r1. The frequency was adjusted again so the transient period could be seen (see Figure 4).

Figure 4
Inductance Transient (RL circuit)
Voltage vs. Time
Time (ms)
Voltage (V)
r1 (Ω)	r2 (Ω)	L (mH)
3.3	99	10

Resonance:

A resistor, inductor, and capacitor was connected in series, and a sinusoid was used as the input voltage. The output voltage (at the resistor) was sampled at different input frequencies surrounding the theoretical frequency (see Figure 4). The experimental frequency could not be determined with any confidence, because there was too much noise and the peak output voltage did not change for a wide band of frequencies.

R (Ω)	L (mH)	C (μF)	Theoretical Resonance Frequency (kHz)
99	1	1	5.03

Figure 4
Resonance (RLC circuit)
Voltage vs. Frequency
Frequency (kHz)
Output peak-to-peak (V)

Analysis:

Ohms Law:

Figure 1 shows the function I=V/R, where V and I are the independent variables, and 1/R is the slope. By performing a linear regression on that data, we obtain the R and its uncertainty (filled in below). r||R is also experimentally determined by using the equation:
"r||R" = rR over {r + R}

	Resistance (Ω)		% diff	Uncertainty (Ω)		% diff
	Theoretical	Experimental		Theoretical	Experimental
r	99.00	N/A	N/A	5.00e-1	N/A	N/A
R	992.00	988.80	0.32%	5.00e-1	4.63e-1	7.30%
r||R	90.00	90.02	0.02%	5.83e-2	5.63e-2	3.58%

The experimental values of the resistances are very close to their theoretical values. The small difference may have resulted from different temperatures of the resistors at different measurement times.

Diode:
I0, defined as the current when V=-%infinite , is zero for the data we obtained. Therefore, the function I(V) = I_0(e^{abs e V / (nk_b T)}-1) could not be modeled.

Copper Wire:

Figure 5
Copper Wire
Temperature vs. Resistance
Resistance (Ohms)
Temperature (K)

%irho(T) = %irho_{0} + AT

A	%irho_{0} (K)
24.55	32.82

resistivity = resistance times {area over length}
length = {mass} over {area times density}

Resistivity (Ω∙m) at T=293K		% different
Theoretical	Experimental
1.70e-6	1.95e-6	14.51%

Diameter (cm)	Density (g/cm3)	Mass (g)	Length (cm)
5.33e-2	8.92	241.8	12.15e4

Capacitor Transient:

The experimental time constant may have been slightly larger than the theoretical time constant because of internal resistance of the voltage source that was not accounted for. Also, before the final measurement was selected, many measurements were taken beforehand, so increased temperature might have affected the overall resistance.
%tau = RC
Figure 6
Capacitor Linearized
ln(Vb-V) vs. Time
Time (seconds)
ln(Vb-V)
RC time constant (seconds)		% different
Theoretical	Experimental
9.85e-3	10.68e-3	8.43%

Inductor Transient:

After linearization, the inductor voltage graph still curved upward towards the end, so only the first half of the transient period was used (Figure 7 below). Furthermore, as seen in Figure 4, the inductor never reaches zero volts. This is because the internal resistance of the inductor has not been accounted for.

%tau = L over R
Figure 7
Inductance Linearized
ln(V) vs. Time
Time (seconds)
ln(V)
RL time constant (seconds)		% different
Theoretical	Experimental
1.01e-4	1.32e-4	30.58%

Resonance:

The resonant frequency was predicted, then we attempted to measure it, but the range of frequencies at peak voltage was very wide. Fortunately, the theoretical resonant frequency was within that range.

The bold horizontal line in Figure 4 marks f_res over sqrt{2} = 1.73 "kHz" . However, not enough samples were taken to find both intercepts (namely, f1 and f2), so a value of Q could not be determined. Instead, the upper bound of Q (Qmax) can be determined using the lower bound of f2-f1.

Q_"max" = f_res over {f_"right"-f_"left"} = 5.3 over {2.32-1.92} = 13.25 and Q <= Q_"max" .

Conclusion:
Ohms law has been successfully demonstrated using simple series and parallel circuits. The rectifier diode could not be modeled, but to some extent a non-ohmic response was demonstrated (exponential response rather than linear). With the copper wire, it was shown how temperature can affect a material's resistivity.

In part 2 of the lab, the transient states of RC and RL circuits were observed. With the RC circuit, the time constant was predicted within 10%, but the time constant of the RL circuit was off by 30% because the internal resistance of the inductor was not considered. Finally, the resonance circuit was relatively inconclusive because the resonant frequency could not be accurately measured and the ratio Q could not be determined, but the graph shows an obvious peak representing resonance.