EN-4000TM4G LTE Broadband Router Is Highly Secure, Flexible, and Reliable

The EN-4000 TM router family adds speed, capacity, and flexibility to the capabilities to Encore Networks’ series of wireline/wireless routers.  This compact IP + Legacy router incorporates Encore’s experience with wired, fiber, and cellular uplinks;  support for numerous data protocols;  and complete remote management.

Designed for commercial and industrial and environments and a wide range of operating ambient temperatures, the all-metal enclosure resists dust, moisture, and electromagnetic interference (EMI), providing Internet Protocol (IP), VPN, Firewall, Ethernet Switching and Legacy Protocol to IP interworking all in a single box solution. The EN4000 is supports a wide range of services and applications used for M2M, SCADA, Smart Grid, and Enterprise applications.

The EN-4000 router base configuration contains a cellular module and five Ethernet ports.  Three expansion slots, two in the front and one internal, accept optional hardware modules (see Table 1).  Expansion slots enhance flexibility and let the EN-4000 router adapt  easily to specific user needs by adding additional Ethernet ports (up to nine total), 3G and 4G LTE cellular modules, encryption hardware, DSP, T-1/E-1 CSU interfaces, fiber optical links, Wi-Fi, a modem behind an FXS analog telephone interface, and serial data ports.

The EN-4000 router supports multiple ports and high-speed network connections while converting legacy protocols, performing routing and switching of network packets, and Layer 4  Firewall and other cyber and physical security measures.

With an embedded Wi-Fi the EN4000 operates as either a router or an access point.

An internal switch, in addition to routing features, allows the EN-4000 router to assign ports to different networks (wired or wireless) and functions (SCADA vs. video). Multiple WAN connections may load share or apply enhanced traffic grooming using QoS and CoS traffic typesassigned to specific links.  Upon a link failure, traffic moves automatically to a working link or to a new connection as programmed.  Simultaneous connections to multiple wireless carriers are a configuration option.

EN-4000 routers draw extremely low power, with typical configurations less than 13 W  Absence of fans or moving parts, increases reliability. Operating temperature range is -40c to +85 C.

Summary Points

- Automatic Failover and load sharing between wireline and wireless links

- Redundant power sources:  AC, DC, or  Power over Ethernet

- Industrial-hardened cyber security appliance and router

- IP Security (IPsec) AES 256 and 3DES

- SSL/TLS encrypted link to the wide area network

- Selective Layer Encryption (Patented) for satellite circuit optimization

- Operation, Administration, and Management (OA&M) with SNMP <might want to point out that it does more than monitor]

- Provides service over any port and any network (IP/MPLS, Cellular 3G , 4G LTE, Frame Relay, circuit switched) Optional WAN interfaces:  3G, 4G LTE cellular, T-1 CSU, serial, Ethernet, optical fiber, analog modem Wi-Fi, and Bluetooth connectivity

- Up to four serial ports for legacy data traffic support

- External Alarm Ports (dry contact sensing, voltage sensing inputs, dry contact closure outputs)

- Legacy protocol support--serial and IP conversion/interworking

TECHNICAL SPECIFICATIONS

| General Features | Protocol management and translation (spoofing) for dozens of protocols |
| --- | --- |
|  | NERC CIP (003, 005, 007, 009) |
|  | Firewall Layer 4 <ELIOS still has unique value] |
|  | Secure wireless connection (encrypted) over public or private cellular network |
|  | SNMPv3 manageability (monitor and configure) |
|  | Up to four antennas handle 3G/4G/LTE cellular, Wi-Fi, and GPS services. |
|  | Access for control via SSH, Telnet, and web access interface |
|  | Three slots for optional interface modules |
|  | Configuration servers to manage and update routers centrally |
|  | Disaster Recovery and Load Sharing over WAN connections |
|  | QoS enforcement to prioritize critical traffic |
|  | Redundant power sources |
| Security Appliance Features | Stateful inspection firewall/ |
|  | WPA IEEE 802.11i (WPA2, RSN) |
|  | DMZ LAN port |
|  | NAT (Network Address Translation) |
|  | SSL/TLS1 |
|  | SSH |
|  | IP Sec (RFC 2401) with AES (128, 192, 256-bit keys) and 3DES |
|  | Generic Router Encapsulation (RFC 1701) |
|  | Internet Key Exchange--IKE (RFC-2409) |
|  | RADIUS authentication |
| Transport Protocols | WAN | IP over Ethernet (compatible with MPLS services) |
|  |  | MPLS compatible |
|  |  | Frame Relay (RFC-1490, IP over FR) |
|  |  | T-1/CSU full or fractional |
|  |  | Asynchronous PPP |
|  |  | Synchronous PPP |
|  |  | X.25 |
|  |  | MLPPP |
|  |  | PPPoE |
|  |  | Selective Layer Encryption (SLE) VPN Optimization (patented) |
|  | IP | IP Versions 4 and 6 |
|  |  | IP Routing (RIP v1/v2), OSPF, BGP, or static routing |
|  |  | DHCP client/server/BootP/Relay |
|  |  | IP QoS and traffic prioritization |
|  |  | IP fragmentation/reassembly |
|  |  | IP routing over VPN; TCP and UDP |
|  |  | 802.1q VLAN tagging |
|  |  | Virtual Redundant Routing Protocol (VRRP) between two routers |
|  |  | Dead Peer Detection |
| Serial Data Support | Up to 4 serial ports supporting V.35, EIA/TIA RS-485, RS-232, RS-422 |
|  | <Is this not true????] |
|  | Legacy Protocol support for DNP3, IEC 60870-5-101/103/104 MODBUS, CDC, S/NET, CONITEL, ABB, X.25, ALC, and most industry proprietary protocols; Inquire about additional protocols |
| Physical Features | EN-4000 Front Panel | 4 LEDs for module ,system status and power indication |
|  |  | One USB host port |
|  |  | Two antenna connectors for internal wireless modules |
|  |  | 2 groups of 4 LEDs for wireless signal strength indication for two cellular modules |
|  |  | <deleting this leaves a hole in the photo unexplained] |
|  | EN-4000 Back Panel | Two antenna connectors for factory-installed internal radios | Cellular: 3G, EVDO, 4G LTE |
|  |  |  | Wi-Fi |
|  |  |  | Bluetooth |
|  |  | One 10/100 Mbit/s Ethernet RJ-45 (WAN); draws PoE with optional PSU |
|  |  | Four 10/100 Mbit/s switched Ethernet RJ-45 (LAN) |
|  |  | 5 V DC input (from AC line-power adapter); factory settable to other DC voltages |
|  | Single Optical Ethernet (Small Form factor Plugable (SFP) interface, for fiber, 1 Gig/s) |
| Optional Modules | Dual Optical Ethernet (Small Form-factor Plugable (SFP) interface, for fiber, 100 Mbit/s) |
|  | Single T1 CSU; channelized/unchannelized/fractional |
|  | 10/100/1000 Mbit/s Ethernet over copper |
|  | 4-Wire E&M (Types 1, 5) |
|  | Dual high-speed serial ports (RS-232, RS-485, RS-422) |
|  | Single V.35 serial port |
|  | V.90/92 modem, FXS port, PPP support (PAP/CHAP) |
|  | One each of FXS and FXO analog ports |
|  | Dual FXS Port |
|  | Digital Signal Processor (DSP) |
|  | Cellular (3G or 4G LTE); CDMA (1xRTT), EVDO, GSM, GPRS, EDGE, UMTS, HSDPA, HSPA |
|  | Wi-Fi |
|  | Bluetooth |
|  | Commercial miniPCI modules such as the latest Wi-Fi |
|  | Hardware Encryption for over 1000 sessions for central site VPN terminations |
|  | Four alarm voltage sensor inputs plus three contact closure outputs |
| Management | SNMP v3 |
|  | Craft Interface |
|  | GUI Web Management |
|  | Telenet |
|  | SSH |
|  | Syslog |
| Power Supply Options | 13 Watts maximum <<isn't this the place to mention power redundancy??] |
|  | DC: 12,24,or 48 V DC |
|  | AC: 100-240 V AC Auto ranging adapter, 50-60 Hz |
|  | Power over Ethernet (Class 3 PoE) |
| Environmental | Operating: -40 C to +85 C (utility hardened) -30 C to +70 C (commercial) |
|  | Storage: -40°C to +85°C |
|  | Humidity: 5% to 95%, non-condensing |
| Mechanical | Height: 1.6 inches/40 mm |
|  | Width: 5.7 inches/145 mm |
|  | Depth: 4 inches/100 mm |
|  | Weight: 1 lb. ( 0.45 kg) |
| Standards Compliance | RoHS Compliant |
|  | EMC | FCC Part 15 |
|  |  | EN 55011/CISPR II |
|  |  | IEC 61850-3 |
|  |  | IEEE 1613 |
|  | Product Safety | UL/CSA 60950-1 |
|  |  | CAN/CSA-C22.2 No. 60950-1-03 |
|  |  | EN 60950-1 |
| Part Number |  |

Table 1:  Feature Module Locations and Installation Options

| Field or Factory Installable modules in Compatible Option Slots |
| --- |
| Slot: | 1 | 2 | 3 |
| 3G/4GLTE radio |  |  |  |
| 802.11 Wi-Fi radio |  |  |  |
| 900 MHz radio |  |  |  |
| Zigbee radio |  |  |  |
| One 10/100/1000T Mbit/s wired Ethernet |  |  |  |
| Single 100FX fiber port (SPF) |  |  |  |
| Dual 100FX fiber port (SPF) |  |  |  |
| One Gigabit Ethernet fiber port (SPF) |  |  |  |
| Two sync/async serial ports; RS-485, RS-232, RS-422 |  |  |  |
| 4-Wire E&M port |  |  |  |
| V.35 serial port, sync/async |  |  |  |
| High-speed DSL modem |  |  |  |
| One T-1/E-1 CSU/DSU, provides both channelized and unchannelized services |  |  |  |
| V.29 modem/FXS |  |  |  |
| Two FXS analog ports |  |  |  |
| FXS and FXO ports, one each |  |  |  |
| 4 Voltage sensors in, 3 contact closures out |  |  |  |
| Hardware encryption |  |  |  |
| Factory Installed Options Soldered onto Main Board |
| PoE receiver, DC input PSU | Requires own back panel. |
| 3G/4G LTE radio | Placed on main board; highest ambient temperature rating. May use two antennas. |
| 802.11b/g/n Wi-Fi radio | Occupies one or two antenna connectors on panel. |
| BlueTooth radio | Option with Wi-Fi feature; shares Wi-Fi antenna |
| Power Failure Alert Module | Dedicated board position |

# Comments

It does more than M2M

Can the main processor perform encryption on ots own???

Reply to Scott (12/10/2012, 14:39): "..."

yes, but with much less capacity.

Can the main processor perform encryption on ots own???

“firewall” listed elsewhere not part of NERC

Do we support v1, v2 and v3?

VPN listed below

VLAN Tagging is not a security feature

We have Wi-Fi what are the security features?

Reply to Scott (12/10/2012, 14:39): "..."

WPA2 is the best encryption available in standard WiFi

Number of VPN is not a security feature. Plus IPSec listed below

AES is the leading technology . 3DES not as popoular

Recommend removing “compatiable with MPLS) With a Linux platform it should support MPLS edge features/

List RFC

Recommend have a NorthAmerican variant only

Reply to Scott (12/10/2012, 14:39): "..."

AFAIK both T-1 and E-1 are configurable on the same chip.

We do not accelerate TCP traffic over satellite

Reply to Scott (12/10/2012, 14:39): "..."

...allows TCP acceleration over high-latency circuits"

Will it do translation?

Recommend just listing the options

Used for what????

Reply to Scott (12/10/2012, 14:39): "..."

modem, voice encoding, etc.

How many end points does it support

Too much info. Implies that the main processors is unable to handle it

Reply to Scott (12/10/2012, 14:39): "..."

can clarify

Added Management

Should have inches as well.

Table 1 Font should be the same as the specification sheet above

Recommend removing reference to “slot” type PCI , Custom, etc

Reply to Scott (12/10/2012, 14:39): "..."

Existence of pure standard miniPCIe slot opens the router to COTS modules.