Change History
Date	Version	Comments
23. July 2012	0.1	Initial Version

# Introduction
# Hardware Interface
## PCI Express Interface
Signal Name	Pad	Direction	Description
HDIN_N0	B14	Input	PCIexpress differential, negative input. This pin must be connected to the PETn0 pin on the PCIexpress card connector
HDIN_P0	A14	Input	PCIexpress differential, positive input. This pin must be connected to the PETp0 pin on the PCIexpress card connector
HDOUT_N0	B11	Output	PCIexpress differential, negative output. An AC-coupling capacitor (75nF to 200 nF) must be placed between this pin and the PERn0 pin on the PCIexpress card connector.
HDOUT_P0	A11	Output	PCIexpress differential, positive output. An AC-coupling capacitor (75nF to 200 nF) must be placed between this pin and the PERp0 pin on the PCIexpress card connector.
REFCLK_N	D8	Input	100 MHz PCIexpress reference clock, negative input
REFCLK_P	D9	Input	100 MHz PCIexpress reference clock, positive input
PERST_N	G13	Input	Active low reset signal from PCIexpress connector.

## FPGA Configuration Interface
Signal Name	Pad	Direction	Description
BUSY / SISPI	K14	Output	Drives the serial data input to the SPI flash memory
CCLK	N11	Bidir.	SPI clock signal. Configured as an output if FPGA is SPI master. Configured as in input otherwise
CFG0	P13	Input	Configuration Mode Pins. These pins are sampled on the rising edge of INITN and set the configuration mode of the ECP2M device. For detailed description, refer to the Lattice ECP2M Family Handbook. / CFG[2:0] Configuration Mode Comments / 0b000 SPI Mode Fast mode if SPIFASTN tied low / 0b010 SPI Dual Image Fast mode if SPIFASTN tied low / 0b101 Slave Serial / 0b111 Slave Parallel / The VIM-PCIe FPGA uses SPI Dual Image mode with SPIFASTN tied high.
CFG1	L10	Input
CFG2	L11	Input
CSN	N14	Input	Only used in parallel load mode. Not used by VIM-PCIe FPGA
CS1N	M13	Input	Only used in parallel load mode. Not used by VIM-PCIe FPGA
D[0] / SPIFASTN	N15	Bidir.	In parallel load mode, this is the data bus LSB. In serial load mode, this port is an input and is used to select fast or normal speed SPI. This input is tied high on the VIM-PCIe FPGA board.
D[1]	N16	Bidir.	In parallel load mode, this is bit 1 of the data bus. Not used by VIM-PCIe FPGA
D[2]	M16	Bidir.	In parallel load mode, this is bit 2 of the data bus. Not used by VIM-PCIe FPGA
D[3]	L12	Bidir.	In parallel load mode, this is bit 3 of the data bus. Not used by VIM-PCIe FPGA
D[4]	L13	Bidir.	In parallel load mode, this is bit 4 of the data bus. Not used by VIM-PCIe FPGA
D[5]	L16	Bidir.	In parallel load mode, this is bit 5 of the data bus. Not used by VIM-PCIe FPGA
D[6]	K16	Bidir.	In parallel load mode, this is bit 6 of the data bus. Not used by VIM-PCIe FPGA
D[7]	L14	Bidir.	In parallel load mode, this is bit 7 of the data bus. Not used by VIM-PCIe FPGA
DI / CSSPI0N	L15	Output	Drives the active low chip select to the SPI flash memory
DONE	N13	Bidir.	This pin is driven low by the FPGA while the initialisation (load) sequence is active and driven high when the initialisation sequence is complete. It can be driven low by an external source to delay the FPGA active state
DOUT / CSON	K13	Input	Data out in bypass mode. Not used by VIM-PCIe FPGA
INITN	M11	Bidir.	This pin is driven low by the FPGA after power-on reset while the configuration is being initialised. It is driven high by the FPGA when configuration completes and before the FPGA starts loading from the SPI flash. INITN can be driven low be external circuitry to delay loading from SPI flash.
PROGRAMN	N12	Input	This input can be pulsed low to initiate device configuration.
TCK	K6	Input	JTAG test clock input
TDI	L5	Input	JTAG test data input
TDO	N6	Output	JTAG test data output
TMS	N4	Input	JTAG test control input
XRES	F4	Input	ECP2M devices require a 10KOhm resistor on the XRES input.

# Software Interface
## PCI Express Configuration Space
31		15	0	Address
Device ID (0x)		Vendor ID (0x)		0x00
Status Register		Command Register		0x04
Class Code (0x)			Rev. ID (0x01)	0x08
BIST (0x00)	Header Type (0x00)	Latency Timer (0x00)	Cache Line (0x00)	0x0C
Base Address Register 0 (0x) :				0x10
Base Address Register 1 (0x) :				0x14
Base Address Register 2 (0x) :				0x18
Base Address Register 3 (0x) :				0x1C
Base Address Register 4 (0x) :				0x20
Base Address Register 5 (0x) :				0x24
Cardbus CIS Pointer (0x0000_0000)				0x28
Subsystem ID (0x)		Subvendor ID (0x)		0x2C
Expansion ROM Base Address (0x0000_0000)				0x30
Reserved			Cap. List Pointer	0x34
Reserved				0x38
Max. Latency (0x00)	Min. Grant (0x00)	Interrupt Pin (0x01)	Interrupt Line	0x3C

Table 1: Configuration Space Header

## Programming Interface
### General Registers
31			15	0	Address
Region ID	Device Status				0x00
Device Control					0x04
Interrupt Status Register					0x08
Interrupt Control Register					0x0C
Real-Time Clock					0x10
Reserved					0x14
Reserved			Reserved		0x18

Table 2 : Overview: General Registers

#### Device Control Register
31	30	29	28	27	26	25	24
-	-	-	-	-	-	-	-

23	22	21	20	19	18	17	16
-	-	-	-	-	-	-	-

15	14	13	12	11	10	9	8
-	-	-	-	PCI_BRK_32DW	PCI_BRK_EN	PCI_NO_SNOOP	PCI_FLUSH_EN

7	6	5	4	3	2	1	0
DSP_EMUL_SEL		-	-	-	INT_CLR	STATE_CLR	DEVICE_RST

DEVICE_RST	Writing a one to this field resets the device transaction layer. The wishbone wrapper containing the PCIexpress IP-core is not reset.