Faculty of Electrical Engineering
University of West Bohemia
Czech Republic
Air Gap Heat Transmission
and Its Consideration in FEM Analyses
Roman Pechanek, Vladimir Kindl, Karel Hruska

---
Presentation Overview
Introduction
Modelling of Air Gap Substituting Thermal
Conductivity
Air Gap Heat Transfer Modelling Using Averaged Temperature in the Air Gap
Theoretical Predictions and Measurement
Conclusion

---
Introduction
- Calculation of heat dissipation in electric machine
  - Thermal network
  - Finite element method
- Both methodologies consider air gap heat transfer

---
Introduction
- Modelling possibilities in FEM
  - Substitution by thermal conductivity
  - Substitution by averaged temperature boundary
- Modelled in ANSYS and compared with measurement

---
Presentation Overview
Introduction
Modelling of Air Gap Substituting Thermal
Conductivity
Air Gap Heat Transfer Modelling Using Averaged Temperature in the Air Gap
Conclusion

---
Modelling Using Averaged Temperature
- The air gap is modelled by an unreal “medium”
- Real air gap
  - Thermal conductivity
  - Heat transfer coefficient
- Model “medium”
  - Thermal conductivity
  - Infinite heat transfer coefficient
- Well definition of the “medium”
  needs empiric values

---
Presentation Overview
Introduction
Modelling of Air Gap Substituting Thermal
Conductivity
Air Gap Heat Transfer Modelling Using Averaged Temperature in the Air Gap
Conclusion

---
Thermal Conductivity Substitution
- The air gap is modelled by a boundary
- No mesh present in the air gap
- The “air gap boundary”
  - The temperature is average
    of both stator and rotor temperatures
  - Pre-calculated heat transfer coefficient
- Does not require
  previously measured values

---
Presentation Overview
Introduction
Modelling of Air Gap Substituting Thermal
Conductivity
Air Gap Heat Transfer Modelling Using Averaged Temperature in the Air Gap
Conclusion

---
- Preliminary calculations
  - Thermal network
  - Machines substitution diagram
  - Prediction of machine's working point

---
- Coupled Electro-Thermal Finite Element Analyses
  - Used previously calculated results
  - Two sets of coupled FEM analyses

---
- Measurement
  - Machinery consisting SIEMENS IM and DC machine
  - Measured temperature of the cast frame

---
Presentation Overview
Introduction
Modelling of Air Gap Substituting Thermal
Conductivity
Air Gap Heat Transfer Modelling Using Averaged Temperature in the Air Gap
Conclusion

---
Conclusion
- Modelling of Air Gap Substituting Thermal Conductivity
  - Provides overshoot in transient phenomenon
  - Requires more elements in FEM models
  - Requires empirically obtained input properties
- Heat Transfer Modelling Using Averaged Temperature
  - Reduces amount of elements in FEM model
  - Does not produce overshoot in transient phenomenon
- Both approaches provide similar results in steady-state

---
Faculty of Electrical Engineering
University of West Bohemia
Czech Republic
rpechane@kev.zcu.cz
vkindl@kev.zcu.cz
khruska@kev.zcu.cz
Address:	Univerzitni 26	Phone:	+420 377 634 101
306 14 Pilsen	Fax:	+420 377 634 002
Czech Republic	E-mail:	rice@rice.zcu.cz