# How to - example

Due to an overwhelming response to our category 5 & 6 tutorial, and many requests for information and wiring diagrams of "straight through" and "crossover" (cross-pinned) patch cords, I have made this informational page.

### Notes for wiring diagrams above:

- For patch cables, 568-B wiring is by far, the most common method.

- There is no difference in connectivity between 568B and 568A cables. Either wiring should work fine on any system*. (*see notes below)

- For a straight through cable, wire both ends identical.

### Patch Cable Assembly Instructions

### Notes Regarding Making Category 5 Patch Cable

1) The RJ-45 plugs are normally made for either solid conductors or stranded conductors. It is very important to be sure that the plug that you use matches the conductor type. It is extremely difficult to tell the difference between the two by looking at them. When you buy these plugs, be sure to categorize, and store them carefully. Using the wrong type can cause intermittent problems. The RJ-45, 8 Conductor Plugs that we sell are rated for both Solid and Stranded cable.

### Controversies and Caveats: Category 5, 5E, and Cat 6 Patch Cables

#### 568B vs. 568A

For patch cables, 568-B wiring is by far, the most common wiring method. Virtually all pre-assembled patch cables are wired to the B standard. There is no difference in connectivity between 568B and 568A cables. Therefore, a 568B patch cable should work fine on a 568A cabling system, and visa-versa. To my knowledge, there has never been an issue with networks of up to 100 megabits. However, with the advent of Gigabit over copper cabling, it may very well become a factor at some point. We have conferred with several cable manufacturers, and many other technical resources, on this subject. The consensus is that mixing of the standards on patch cables should not cause a problem. Since Gigabit networks over copper cabling are in their infancy, and no one can say for sure, we would advise our customers to take the safe approach on all future patch cable orders. We now offer our custom cat 5E and category 6 cables in both 568A and 568B wiring schemes for this reason.