SERVICE MANUAL

3AB1 ISUZU ENGINE

S/V Kuan Yin

April 2014
Contents

Overview	page
Engine
Fuel
Oil
Coolant

Engine
Engine Serial Number
1) Located on the bolt boss, left side of the bell housing, after of the starter motor.
2) The number has 5 (or 6) digits.
First:	year of manufacture. ie. 2 is 1972.
Second:	number of cylinders.
Third-Fifth:	engine number
Parts
1) All part numbers have five digits. (These are Isuzu Pisces instructions).
First:	section of the parts book
Second:	number of cylinders
Third -Fifth:	part number

Section	Number Series	Description
0	00000	Bolts – nuts - washers
1	10000	Bellhousing components
2	20000	Lubrication system
3	30000	Cooling system
4	40000	Fuel system
5	50000	Exhaust system
6	60000	Electrical system
7	70000	Mounting System
8	80000	Basic Engine Parts
9	90000	Accessories

Engine
Engine Type	4-cycle,
water cooled
overhead valve (OHV)
in-line
swirl chamber
integral (no liner)
Engine Rotation	standard (CCW @ flywheel, CW @ front timing gear)
Max Engine Inclination	150
Torque (maximum)	75.95 ft/lbs	10.5 kg-m/2000 rpm
Horsepower	40 @ 2800 rpm

Idle Speed	700 rpm
Dry weight	217 kg (477.4 lbs)
Size	653 mm x 515 mm x 693 mm
(25.71” x 20.28” x 27.28”)

Firing Order	1 – 3 – 2
Piston displacement	1777 cc (108.5 in3)
Cylinders	3 – 86 mm x 102 mm (3.39” x 4.02”)
Compression pressure	>minimum 20 kg/cm2	(< = overhaul required)
Compression ratio	20 : 1

Rated output

PS/rpm	governed hp	fuel
hp	consumption
18.5	1400
25.0	1800
31.0	2200
33.0	2400
36.0	2600
38.0	2800

Starter (original)	12V – 1.8kW
Air Cleaner	not equipped

Fuel
Injection pump	Reformed Bosch, in-line
NP-PES-3A 65B
Kiki Diesel under license from Bosch
pump assembly #1342-004
Injector nozzle type	NP-ONOSD211
Injector opening pressure	1706 psi (120 kg/cm2)
Injection Timing @ 1000 rpm	180

Fuel consumption	210g/PS-h @ full load = 285.5208 g/kWh

Governor	all speed mechanical type
Governor setting rpm	2800

Engine Oil
Engine oil quality	Series 3 API Spec CD or above
Oil viscosity	)	> 26.70C (800F) SAE 40
ambient temp.	)	< 26.70C (800F) SAE 30
)	> -150C SAE 15W40, SAE 15W50
Oil capacity	4.8 L (5 quarts)
6.2 L
Oil pump type	trochoid type
Oil delivery	>13 L/min
Oil pressure, warm engine	idle	25 – 50 (1.75 – 3.51 kg/cm)
full speed	40 – 60 (2.81 – 4.21 kg/cm)
Pump speed	1000 rpm
Pressure of delivery	4 kg/cm2
Oil temperature	50 0C
Oil filter type	full-flow with paper element
Oil filter relief valve opening pressure	4.2 – 4.7 kg/cm2	59.7 – 66. 8 psi (system relief to oil pan)
Oil overflow valve opening pressure	0.8 – 1.2 kg/cm2 11.4 – 17.1 psi (clogged filter)

Coolant
Cooling type	raw water/closed loop coolant
Coolant capacity	6.5L (7 quarts)
Thermostat	begins to open	800C (1760F)
fully open	880C (1900F)
Raw Water Pump	1/2” neoprene impeller

Valves
Valve clearance, cold	intake & exhaust	0.018” (0.45mm)
Valves sequence:
Cylinder number	1	3	3
Valve arrangement	I E	E I	I E
Cyl #1 at TDC	0 0	0	0
Cyl #1 at BDC	-	0	0

Oil Pump
Clearance rotor, vane and cover	standard	0.02 – 0.07 mm
need service	0.15 mm
Tip Clearance rotor and vane	standard	0.02 – 0.13 mm
Clearance rotor tips and pump body	standard	0.02 – 0.27 mm
Clearance rotor shaft and pump body	standard	0.04 mm
need service	0.2 mm

Coolant pump

Thermostat	Wax-pellet type with by-pass
Thermostat	opens	76.5 ± 1.5 0 C
Valve lift (@ 90 0 C	8.0 mm
Closed to fully open	by 87 0 C, 3 – 5 minutes to respond
Type of seal	impeller type with 6 blades, cast with iron
Pump delivery	60 L/min
Pump speed	3000 rpm
Head	2.5 m
Type of seal	mechanical seal
Type of bearing	ball
Pulley diameter	114 mm
Pulley ratio (crankshaft : pump	1.2:1
Coolant capacity	4.4 L

Injectors (nozzle)
Bosch throttle type
Orifice	1 mm diameter
Spray angle	00
Adjusted with screw to	120 kg/cm2
Test for leakage	apply 100 kg/cm2
apply 300 kg/cm2 by turning screw
drops from 250 to 200	<5 secs	replace nozzle assembly

Fuel Filter

Glow Plugs
Rated Voltage	10.5 v
Rated Current	6.5 (+1 – 0.5) A
Isuzu part number	8521-1957
Manufacturer's PN	AKE/GS10/19B-2

Maintenance Chart

Operation	Adjustment	Period	Hours
		Daily	Weekly	100 hr	300 hr	600hr
Engine oil	check level	X
Injection Pump Oil	check level	X
Transmission Oil	feel case for oil	X
	check level		X
Engine oil AND filter	change			X
Injection Pump Oil	change 200 hours			X	X
Transmission Oil	drain and change			X
Injector	check pressure & spray				X
2nd fuel filter (on engine)	change 2µm element			X
2nd fuel filter	open drain plug			X
Fuel pump filter	clean strainer				X
Alternator belt	check tension ± 5mm	X
Prop shaft coupling	check bolts	X
Primary fuel filter	Check bowl for water		X
Primary fuel filter	change 10µm element	gauge	falls	to	Yellow
Engine mounts	check condition				X
Valve clearance	check = .018” .45mm				X
Air cleaner	clean			X
Engine coolant	check level	X
Engine coolant	check with hydrometer			X
Engine coolant	flush and change				season
Heat exchanger	check anode				season
Control cables (teleflex)	lubricate			X
Raw water impeller	check for leakage	X
Raw water impeller	Check impeller				season

Maintenance

Fuel Filter
1) open drain plug on bottom of secondary fuel filter to drain any water every 100 hours.
2) Replace fuel filter element every 200 hours.

Remove the filter element
1) Clean outside of filter assembly.
2) Shut of fuel supply valve.
3) unscrew the centre pipe and remove the cover, filter body and element.
4) NOTE: Take care not to lose the spring and the two flat washers located at each end of the element.
5) Remove the inlet banjo bolt and clean the fuel strainer.
6) Reinstall the bolt and strainer.
7) Install a new element and bleed air from the system.

Bleeding the fuel system
1) Opened the fuel supply valve.
2) Loosen the air bleed screw at the side on top of the secondary fuel filter (NOT the screw in the centre of the top of the filter assembly).
3) operate the manual primer pump until fuel flows freely from the filter bleed plug.
4) Close the plug on the fuel filter.
5) Opened the air bleed screw on the injection pump.
6) Operate the primer pump until fuel flows free of air bubbles.
7) Close the air bleed screw on the injection pump.
8) Push down and twist lock the manual primer pump plunger.

9) If the engine fails to start, or runs unevenly, loosen the high pressure fuel lines at the injectors.
10) Pull engine stop solenoid to ensure engine will not start.
11) open the throttle and crank the engine until fuel flowing from the loosened injector lines is free of air.
12) Tighten the injector line fittings.

Injection Pump
1) Oil change every 200 hours or monthly.
2) To drain oil, remove drain plugs located on the bottom of the pump housing and governor housing.
3) Quantity: Approximately 0.16L (0.17 Qt) for governor housing and
0.11L (0.12 Qt) for pump can housing.
4) Quality: Use clean engine oil.
5) Refill both the injection pump cam and governor compartments at breather	openings.
6) Maintain oil level at the indicator line on the dipstick.
7) NOTE: A small amount of diesel fuel will leak past the injection pump plungers to lubricate these parts and will tend to dilate the oil in the injection pump housing. If dilation oil with diesel fuel is excessive, worn fuel injection pump plungers or fuel feed pump push rod should be suspected.

Valve Adjustment
1) Bring #1 piston to TDC on compression stroke.
2) Mark on crankshaft pulley should be aligned with timing pointer.
3) Use feel gauge to check gap on:
#1 intake and exhaust,
#2 intake
#3 exhaust
4) Turner crankshaft one complete revolution until TDC mark is a gain aligned with the timing pointer.
5) Adjust the remaining two valves:
#2 exhaust
#3 intake

Troubleshooting

Hard starting

Pinion gear does not engage flywheel ring gear when starter switch is turned
1) Poor connections between battery, key switch, starter solenoid, starter circuit	momentary switches and starter. Correction: Check all connections for	corrosion,and looseness. Clean and tighten.
2) Armature shaft splines defective causing binding of opinion.
Correction: Correct splines.
3) Plunger of magnetic switch sticking, or coil circuit open or shorted.
Correction: Correct or replace.

Pinion gear engages ring but engine will not turn over
1) Wire between battery and solenoid, or key switch and solenoid, or solenoid and starter motor are poorly connected, or poorly grounded.
Correction: Check connections and tighten or replace.
2) Pinion not engaging ring gear properly. Correction: Correct teeth.
3) Starter motor loose on engine. Correction: Read tighten bolts.
4) Starter motor brushes worn or brush springs in contact with computator face.	Correction: Correct or replace.
5) Computator fouled. Correction: Correct or replace.
6) Armature or field coils are defective. Correction: Correct or replace.
7) Poor connections between field coils and brushes in starter motor.
Correction: Correct or replace.
8) Contact points fouled, or roughened. Correction: Correct or replace.

Pinion spins that before engaging ring gear
1) Plunger gap incorrect (gap "1") Correction: Adjust.
2) Pinion sleeve spring weakened. Correction: Replace.

Pinion gear engages ring gear properly but engine will not turn over
1) Overrunning clutch defective. Correction: Replace.

Starter motor does not stop when starter switch is turned off
1) Internal parts of switch shorted. Correction: Replays switch.
2) Contact points in switch seized. Correction: Replace.

Trouble in the fuel system
refer to fuel system

Trouble in the oil system
1) Sump oil diluted with fuel oil. Excessive diesel fuel may be leaking past the injection pump plungers. Worn fuel injection pump plungers or fuel feed pump push rod should be suspected. Correction: Investigate and replace as necessary.

Engine lacks compression
1) valves poorly seated, or valve stem bent.
Correction: Check valves and valve seats. Lap valve seats as necessary.
2) valve springs weakened or broken. Correction: Replace valve springs.
3) cylinder head gasket defective. Correction: Replace gasket.
4) pistons or piston rings worn excessively:
Correction: replace piston and piston rings.

Engine idles rough
1) Throttle valve poorly adjusted. Correction: Adjust.
2) Fuel injection timing incorrect. Correction: Adjust (see Fuel System p XX)
3) Pneumatic governor poorly adjusted. Correction: Correct (see Fuel System p XX)
4) Air in fuel injection pump. Correction: Bleed fuel injection pump (p XX)

Engine lacks power
`Engine lacks power continuously
1) Valves clearance incorrect. Correction: Adjust.
2) Valves poorly seated. Correction: Refer to para 1-2-3
3) Cylinder head gasket defective. Correction: Replace gasket.
4) Piston rings worn or sticking. Correction: replace piston rings.
5) Fuel injection timing incorrect. Correction: Adjust.
6) Volume of fuel injection insufficient. Correction: Adjust.
7) Pressure of injection incorrect or valve in injection nozzle seized.
Correction: Adjust or replace.
8) Feed pump out of normal function. Correction: Correct.
9) Restrictions in fuel lines. Correction: Correct or replace.
10) amount of intake air insufficient. Correction: service air cleaner
 change oil in air cleaner.
11) Throttle valve sticking or binding. Correction: Correct or replace.
12) Clutch slipping. Correction: Correct.
13) Brake dragging. Correction: Correct.

Engine lacks power while accelerating
1) Engine lacks compression. Correction: see para 1 -3.
2) Fuel injection pattern poor. Correction: Adjust. (See page XX)
3) Injection pump timer out of normal function.
Correction: Correct or replace, see page xx
4) Fuel injection pressure or spray angle incorrect.
Correction: Correct or replace,	see page xx.
5) Feed pump malfunction. Correction: Correct or replace, see page xx.
6) Amount of air intake insufficient.
Correction: Service air cleaner, change oil in air cleaner.
7) Throttle valve not opening wide. Correction: Correct or replace.

Engine overheating
1) Engine oil level too low, or using wrong oil.
 Correction: Replenish, or replace with correct oil.
2) Coolant level too low, restrictions in cooling system are due to formation of scales.	Correction: Replenish or clean system.
3) Pressure valve spring in coolant tank cap weakened.
Correction: Replays filler cap.
4) Loss of coolant. Correction: Check all coolant hoses, heat exchanger and	coolant circulating pump on engine for signs of leak. Correct or replace.
5) Water pump malfunctioning. Correction: Correct or replace.
6) Thermostat defective. Correction: Replace thermostat
7) Fuel injection timing incorrect. Correction: Adjust injection timing.
8) No raw water to heat exchanger. Correction: Check strainer, raw water pump	and hoses.
9) Heat exchanger coolant tubes plugged. Correction: Reverse flush tubes.
10) Valve clearances incorrect. Correction: Adjust valves.
11) Cylinder head gasket defective. Correction: Replays cylinder head gasket.
12) Resistance in exhaust system to high. Correction: Clean or replace.

Engine over-cooling
1) Thermostat not closing. Correction: Replace thermostat.

Engine noisy
Abnormal engine noise often consists of combined noises originating in a rotating and/or sliding parts of the engine. It is, therefore, advisable to check the engine components and associated parts systematically to determine the true source of any abnormal noises.

Crankshaft bearing noise
1) Oil clearances increased due to worn bearings or crankshaft. Correction: Replace bearings or have crankshaft ground.
2) Crankshaft worn. Correction: Replace or have crankshaft ground.
3) Restrictions in oil passages. Correction: Clean oil passages.
4) Bearings seized up. Correction: Replays bearings, or have crankshaft ground.

Connecting-Rod or connecting-rod bearing noise
1) Connecting-rod bearings or worn. Correction: Replace bearings.
2) Crank pins or worn. Correction: Have crankshaft ground.
3) Collecting-rod (s) bent. Correction: Correct or replace connecting-rod(s).
4) Connecting-rod bearings seized up.
Correction: Replays bearings and have crankshaft ground.
5) Connecting-rod bearings poorly lubricated. Correction: Clean oil passages.

Piston, piston pin or piston ring noise
1) Piston clearance increased excessively due to worn Pistons and piston rings.	Correction: Replays Pistons and piston rings.
2) Pistons or piston pins worn. Correction: Replays pistons or piston pins.
3) Piston(s) seized up. Correction: Replays pistons.
4) Piston(s) in for contact with cylinder wall. Correction: Replays pistons.
5) Piston ring(s) damaged. Correction: Replays piston rings.

Cooling system noisy
1) Water pump bearing defective. Correction: Replays bearing, using a repair kit.

Other noises
1) Crankshaft thrust bearings worn. Correction: Replays thrust bearings.
2) Camshaft end play excessive. Correction: Replays thrust plate.
3) Timing gear backlash excessive. Correction: Replays timing gear.
4) Valve clearances excessive. Correction: Adjust valve clearances.
5) Valve lifters worn. Correction: Replays valves.

Fuel consumption excessive
1) Fuel injection timing incorrect. Correction: Adjust.
2) Clutch slipping. Correction: Adjust clutch.

Oil consumption excessive
Oil burning
1) Clearance between a cylinder and Pistons excessive. Correction: Replays pistons	to provide an adequate clearance.
2) Piston rings worn, sticking or broken. Correction: Replays piston rings.
3) Position of piston ring gaps incorrect. Correction: Adjust.
4) Oil return holes in oil rings clogged. Correction: Replace oil rings.
5) Air breather clogged.

Oil leaking past valve stem clearances
1) Clearance between valve stems and valve guides excessive. Correction: Replays valves and valve guide.
2) Cylinder head gasket defective. Correction: Replays gasket.

Oil leakage
1) Hose clamps loose. Correction: Re-tighten.
2) Oil filter leaking. Correction: Re-tighten, or replace.
3) Oil seal defective. Correction: Replace oil seal.

Alternator
No charging taking place
1) Alternator belt loose. Correction: Tighten belt and check alignment.
2) Lose connections on alternator. Correction: Check connections and tighten.
3) Loose connection on battery. Correction: Check connection and tighten.
4) Loose connections on multistage regulator.
Correction: Check connections and tighten.
5) Circuit poorly grounded. Correction: Check connections and tighten.
6) Diodes in alternator failed. Correction: Test diodes in rectifier.
7) Stator coil has failed. Correction: Test continuity and replace if needed.
8) No field/excitor current to excite stator.
Correction: Check wire and replace is needed.
9) Brushes in poor contact with slip rings. Correction:

Battery under-charging
1) Alternator belt slipping. Correction: Tighten the belt and check alignment.
2) Brushes sticking or in poor contact with slip rings. Correction: Re-phase slip	rings. Clean brush holders.
3) Rotor coil shorted. Correction: Correct or replace.
4) State coil open or shorted. Correction: Correct or replace.
5) Diode defective. Correction: Replace.

Charging current unstable
1) Circuit wires poorly connected. Correction: Check and re-tighten.
2) Brushes in poor contact with slip rings. Correction: Correct or replace.
3) Rotor coil open or shorted. Correction: Correct or replace.
4) Stator coil open or shorted. Correction: Correct or replace.
5) Connection between stator coil and diode loosened. Correction: Check and re-	tighten.

Abnormal noise
1) Part loose in alternator mount. Correction: Check and re-tighten.
2) Bearing defective. Correction: Replace.
3) Diode defective. Correction: Replace.
4) Stator coil shorted. Correction: Correct or replace.

Alternator fuse blows (positive to battery)
1) Diodes defective. Correction: Replace.

Winterizing Engine

Engine

Raw Water
1) Drain seawater from raw water filter
2) 1/2 fill with antifreeze
3) Leave seacock OPEN
4) Remove cover plate from impeller pump
5) Remove impeller and check vanes for cracks, damage
6) Grease vane tips with vaseline
7) Store impeller, cover, O-ring and screws in labelled bag
8) Ensure hose from seawater filter is drained
9) Ensure hose from pump to heat exchanger is drained
10) Ensure hose from heat exchanger to North Sea exhaust is drained

Heat Exchanger
1) Remove zinc plug/anode and drain heat exchanger

Transmission

Batteries
1) Clean battery case
2) Check fluid levels
2) Ensure fully charged
3) Disconnect positive AND negative (+ on equipment might have gnd leak)

1	Drive plate – 10 tooth (1) 12405
2	Lock washer 8 mm (9) 02242
3	Bolt M8 1.25 x 20 (3) 02252
4	Bellhousing ZF 12404
5	Lock washer M10 (17) 02342
6	Bolt M10 1.5 x 45 (8) 02357
8	Bolt M10 1.5 x 30 (8) 02354
10	Cable clamp (1) 12151
11	Screw, fillister head 10-32x5/8 (2) 02661
12	Lockwasher #10 (2) 02662
13	Nut 10-32 (2) 02663
25	Foot, engine rear (1) 12420
26	Nut 5/8-18 Marsden 02752
27	Engine mount, flexible (2) 72782
28	Bracket, throttle (1) 12421
    * Isuzu Pisces parts numbers

Oil System (Filter)

Oil System

#	Item	#	Pisces	Isuzu
1	Oil filter bracket	1	22200
2	Lock washer M8	11	02242
3	Bolt M8-1.25x20	2	02252
4	Oil filter backing plate	1	22201
5	Gasket	2	22202
6	Oil filter housing assembly	1	22203
7	Street “L” 3/8 NPT	1	02694
8	Bolt M8-1.25x40	6	02256
9	Hose assembly 17”	1	22211
10	Oil filter	1	22210
11	Inverted flare 3/8NPT-1/2” Hose	2	02721
12	Hose assembly 11 3/4”	1	22212
13	Bolt M8-1.25x50	2	02258
14	Oil bypass block assembly	1	23204
15	O-ring	1	22205
16	Relief valve	1	22206
17	Reducer, bushing 3/4 to 3/8	1	02719

Oil Pipe Assembly & Oil Breather Assembly

Oil Pipe Assembly & Oil Breather Assembly

#	Item	#	Pisces	Isuzu
1	Pipe, oil breather	1	23220
2	Cap, oil breather	1	22221
3	Gasket	1	22222
4	Bolt M8-1.25x15	4	02251
5	Lockwasher M8	4	02242
7	Hose	1	53515
8	Clamp	2	02685
9	Oil tube assembly, rocker feed	1	22261
10	Crush washers	1	22263
11	Hollow bolt	1	22262

Oil Pump Assembly

Oil Pump Assembly

#	Item	QU	Pisces	Isuzu
1	Oil pump assembly	1	22230
2	Rotor & shaft assembly	1	22231
3	Pinion gear	1	22232
4	Pin	1	22233
5	Cover, oil pump	1	22234
6	Bolt M8-1.25x50	2	02258
6	Washer M8	6	02241
6	Bolt, cover M8-1.25x25	2	02253
6	Lockwasher M8	6	02242
7	Oil strainer	1	22239
8	Case	1	22241
9	Bolt M8-1.25x15	1	02251
10	Bolt M8-1.25x25	2	02253
11	Oil pipe assembly	1	22245

Coolant (Engine Water) Pump

Coolant (Engine Water) Pump

#	Item	QU	Pisces	Isuzu
1	Water (coolant) pump assembly	1	32050
2	Plug, heater 3/8 NPT	1	32119
3	Bearing assembly	1	32051
4	Set screw M8 special	1	02652
5	Lockwasher M8	1	02242
6	Retaining ring	1	32052
7	Seal assembly	1	32053
8	Impeller	1	32054
9	Flange	1	32055
10	Cover, rear	1	32056
11	Gasket	1	32057
12	Screw, rear cover	7	32060
13	Gasket	1	32057
14	Kit, water pump repair / items 3, 6, 7, 11, 13	1	92012
16	Bolt M10-1.25x50	4	02784
17	Lockwasher M10	5	02342
18	Bolt M10-1.25x50	1	02785
19	Lockwasher M10	1	02342
20	Tension arm (alternator)	1	62715
21	Pulley	1	32059
22	Bolt M6-1.0x12	4	02184
23	Lockwasher M6	4	02182
24	V-belt	1	32360

Coolant (Engine Water) Inlet Pipe

Coolant (Engine Water) Inlet Pipe

#	Item	QU	Pisces	Isuzu
1	Pipe, water (coolant) inlet	1	33380
2	Hose clamp 20	2	32395
3	Hose 1 3/8 x 7/8	1	32386
4	Adel clamp	1	02757
5	Spacer	1	32387
6	Screw, 10-24x1 TCS	1	02660

Thermostat Assembly

Thermostat Assembly

#	Item	QU	Pisces	Isuzu
1	Housing, lower	1	32114
2	Housing	1	32115
3	Thermostat	1	32118
4	Plug 3/8 NPT	1	32119
5	Gasket	1	32120
6	Bolt M8-1.25x30	2	02254
7	Lockwasher M8	2	02242
8	Temperature Sender	1	62635
9	Gasket	1	32122
10	Bolt M8-1.25x25	4	02253
11	Lockwasher M8	4	02242
12	Flatwasher M8	4	02241
13	Hose, bypass	1	32123
14	(hose) Clamp #8	2	32391

Heat Exchanger Assembly

Heat Exchanger Assembly

#	Item	QU	Pisces	Isuzu
1	Heat exchanger	1	32370
2	Gasket	1	32371
3	Cap	1	32373
4	Bolt, bronze	1	02650
5	Zinc plug assembly	1	52511
5	Zinc (anode)	1	52512
6	Bracket	1	32376
7	(bolt) Clamp #44	2	32401
8	Bolt M10-1.5x25	2	02353
9	Lockwasher M10	2	02342
10	Hose (STBD)	1	32377
11	Hose clamp #16	4	32394
12	Hose (PORT)	1	32378
13	Hose 5/8 x 19” (seawater)	1	33385
14	(hose) Clamp #10	4	32392
15	Plug 1/8 NPT	1	02681
16	Hose 5/8 x 2.87” (seawater)	1	32384

Fuel Injection Pump

Fuel Injection Pump

#	Item	QU	Pisces	Isuzu
	Injection pump assembly	1	43201
1	Delivery valve	3	42214
2	Gasket	3	42262
3	Spring	3	42215
4	Oil seal	1	42271
5	Cam shaft	1	43236
6	Bearing	1	42237
7	Bearing	1	42238
8	Tappet	1	43220
9	Plunger	1	42261
10	Spring	3	43228
11	Gasket	2	42039
12	Holder	3	42216
13	Dip stick	1	43207
14	O-ring	1	42213
15	Bleed screw	2	42248
16	Hollow bolt	1	42246
17	Seal	1	42271
18	O-ring	1	42256
19	Gear	1	82322

Fuel Feed Pump

Fuel Feed Pump

#	Item	QU	Pisces	Isuzu
1	Feed pump assembly	1	43020
2	Piston	1	42021
3	Spring	1	42022
4	Gasket	1	42024
5	Cap plug	1	42023
6	Tappet body	1	42025
7	Guide	2	42028
8	Pin	1	42027
9	Roller tappet	1	42026
10	Snap ring	1	42040
11	Crushwasher	4	42038
12	Filter	1	42036
13	Hollow bolt	1	42035
14	O-ring	2	42023
15	Valve, check	2	42029
16	Spring	2	42030
17	Pump, priming	1	42034
18	Cover, dust	1	42039
19	Hollow bolt	1	42037
20	Adaptor	1	42031
21	O-ring	1	42033

Governor Assembly

Governor Assembly

Injector (Nozzle) Assembly

Injector (Nozzle) Assembly

#	Item	QU	Pisces	Isuzu
1	Nozzle holder assembly w/nozzle	3	42050
2	Push rod	3	42053
3	Spring nozzle	3	42054
4	Screw, spring adjust	3	42055
5	Nut	3	42056
6	Nut screw cap	3	42057
7	Gasket	6	42058
8	Washer	3	42059
9	Nut nozzle	3	42060
10	Washer	3	42061
11	Inlet connector assembly	3	42062
12	Connector, fuel inlet assembly	3	42063
13	Strainer, edge type	3	42064
14	Hollow bolt	3	42065
15	Gasket	6	42066
16	Screw, nozzle holder	3	42067
17	Washer, nozzle holder	3	42068
18	Corrugated washer (copper)	3	42069
19	Nozzle heat shield	3	42070
20	Washer, nozzle shield	3	42071
21	Body, nozzle holder	3	42052
22	Nozzle	3	42051

Fuel Lines

Fuel Lines

#	Item	#	Pisces	Isuzu
1	Injection line #1 cyl	1	42072
2	Injection line #2 cyl	1	42073
3	Injection line #3 cyl	1	43080
5	Clip assembly	2	42075
6	Lockwasher M5	2	02172
7	Screw M5 0.8x20	2	02174
8	Pipe, fuel by-pass (rtn)	1	43074
9	Hollow bolt	1	42017
10	Crushwasher	2	42018
11	Fuel filter assembly	1	42001
12	Injection pump assembly	1	43201

Spin On Fuel Filter

Exhaust Manifold Assembly
(includes coolant reservoir)

Timing Gear Cover

Timing Gear Cover
Cylinder Head

Cylinder Head
Cylinder Block

Cylinder Block
Crankshaft

Crankshaft
Camshaft

Camshaft
Raw Water (sea water) Pump

Starter Motor (original)

Alternator

Front Engine Mount

Engine Specifications

Valves
Rocker arm shaft	normal diameter	19.00 mm
limit for use	18.85 mm

Clearance rocker arm shaft (layshaft) and bushing	standard	0.01 – 0.05 mm
limit for use	0.2 mm

Clearance between valve stem and valve guide
standard (Intake)	0.039 – 0.068
need for service	0.18 mm
standard (Exhaust)	0.064 – 0.093
need for service	0.25 mm

Valve seat contact width	standard (both)	1.2 – 1.5 mm
need for service	>2 mm

Valve seat depression	standard (both)	3.1 mm
need for service	3.6 mm

Valve seat insert
intake grade A ID bore dia.	40.00 – 40.03 mm OD dia.	40.11 – 40.13 mm
 grade B	40.031 – 40.05 mm	40.131 – 40.16

exhaust grade A	34.00 – 34.03 mm	34.11 – 34.13 mm
   grade B	34.031 – 34.05 mm	34.131 – 34.16

Valve head thickness	standard	1.3 mm
limit for use	1.0 mm

Valve seating value	450

Valve springs	deviation from vertical	limit for use	1.5 mm
Valve spring tension	standard free length	46 mm
limit for use	44.5 mm
standard tension @39mm	18.4 – 18.6 mm
limit for use	17.9 mm

Valve clearance (engine cold)
Intake	0.018” (0.45 mm)
Exhaust	0.018” (0.45 mm)

Valve stem diameter (both)	normal diameter	8 mm
limit for use, intake	7.88 mm
limit for use, exhaust	7.85 mm

Tappets	nominal diameter	13 ø
limit for use	12.95 ø

Clearance between tappet and cylinder body	standard	0.1 – 0.4 mm
limit for use	0.1 mm

Hot plugs	maximum allowable depression	0.02 mm

Cylinder Head
Cylinder body	distortion of upper surface	standard	< 0.05 mm
need for service	< 0.2 mm
Cylinder head	lower face	limit of allowable distortion	0.2 mm
correct to within	0.05 mm
Cylinder head	joining face of intake & exhaust manifolds
limit of allowable distortion	0.4 mm
correct to within	0.05 mm
Cylinder bore	standard	86 mm

Pistons
Piston ring gaps	1st, 2nd, 3rd compression rings	standard	0.2 – 0.4 mm
limit for use	1.5 mm

1st and 2nd oil rings	standard	0.1 – 0.3 mm
limit for use	1.0 mm

Piston ring clearance
1st, 2nd compression rings	standard	0.045 – 0.075 mm
limit for use	0.3 mm
3rd compression ring	standard	0.030 – 0.060 mm
limit for use	0.3 mm
1st, 2nd oil rings	standard	0.020 – 0.054 mm
limit for use	0.15 mm

Connecting Rods
Connection Rods	distortion	standard (per 100mm)	< 0.08 mm
need for service	> 0.2 mm
misalignment	standard (per 100 mm)	< 0.05 mm
need service	> 0.15 mm

Connecting rod small-end bushing clearance to piston pin
standard	0.008 – 0.020 mm
limit for use	< 0.0.05 mm

Connecting rod big-end clearance to crankpin	standard	0.18 mm – 0.30 mm
limit for use	> 0.35 mm

Connecting rod oil clearance	standard	0.029 – 0.082 mm
limit for use	> 0.12 mm
Bottom End

Main Journal Bearings
standard diameter	69.92 – 69.93 mm
Oil Clearance	desired	0.019 - 0.064 mm
wear limit for use	0.12 mm
Crankshaft
Crankshaft Nut	15mm
Crankshaft bearings oil clearance	standard	0.019 – 0.064 mm
need service	> 0.12 mm

Crankshaft	nominal diameter of crank journals	70 ø
nominal diameter of crankpins	53 ø
crankpin journal & crankpin finishing accuracy	> 0.007 mm

Crankshaft run out (measured with dial indicator)
standard	< 0.03 mm
need service	> 0.06 mm

Crankshaft thrust clearance	standard	0.04 – 0.198 mm

Crankshaft end play (when installed)	0.04 – 0.198 mm	need service	> 0.30 mm

Camshaft
Camshaft	height of cam lobes	standard	40.6 mm
limit for use	40.2 mm
reduction in dia. camshaft journals	standard	48 mm
limit for use	47.6 mm

Camshaft end play (measured w/feeler gauge)	standard	0.050 – 0.114 mm
need service	> 0.2 mm

Timing Gear backlash	standard	0.1 mm
limit for use	> 0.3 mm

Manifold Assembly distortion	standard	0.05 mm
need service	>0.2 mm

Camshaft end play (when installed)	0.08 mm

Gasket – bearing arch No1 & No3 projection of gasket	0 – 0.05 mm

Governor
Clearance between tappet & pump housing	standard	0.03 – 0.07 mm
limit for use	0.2 mm
Control rack backlash	standard	0.15 mm
limit for use	0.03 mm

Injector nozzle pressure drop
250 to 200 kg/cm2	standard	> 5 seconds
limit for use	< 5 seconds

Plunger Springs Specifications
Spring length when free	51.5 mm
Limit for use	49.5 mm
Length compressed to 44 mm	Replace if spring tension < 13.3 kg
Allowed deviation from vertical	Replace if > 1.5 mm

Injection Pump Control Rack full stroke	standard 21 mm

Alternator
Fan belt deflection (finger pressure)	5 mm

Torque Specifications
Item	FT-lbs	m-kg
Bearing cap bolts	123 ± 7	17 ± 1.0 m-kg
Flywheel bolts	61	8.5 m-kg
Bearing cap bolts	58
Thrust plate bolts	50	7 m-kg
Oil pan bolts	70 INCH/lbs	0.8 m-kg
Crankcase bolts	15	2.1 m-kg
Cylinder head bolts FIRST	22 - 36	3 – 5 m-kg
SECOND	47	6.5 m-kg
(in sequence) THIRD	58 ± 16 (56-60)	8.0 ± 2.5 m-kg
Rocker arm shaft bolts	18	2.5 m-kg
Valve rock arm cover	10
Crankshaft pulley to crankshaft bolt	108	15 m-kg
Injector nozzle holder	54	7.5 m-kg
Connecting rod, bearing cap bolts	57	8 m-kg
Governor – delivery valve holder	22 - 25	3 – 3.5 kg-m
Governor – flyweight nut	36 - 43	5 – 6 kg -m
Injector nozzle nut	43	6 + 2 kg- m
Injection Pump Valve Holder Torque	3→0→3→0→3~3.5 kg-m	3 = 21.7
Inj Pump – lock plate bolts	70 INCH/lbs	0.8 m-kg
Connecting rod bolts	55 - 61
Main bearing cap bolts	116 - 130
Camshaft gear cap screw	80
Cam gear bolt	80
Timing gear cover	14
Camshaft thrust plate	51
Inj. pump delivery valve holder	22 - 25
Inj. Nozzle cap nut	45
Inj. Nozzle retaining nut	54
Water pump mounting bolts	30

Gaskets

rocker cover gasket
cylinder head gasket
arch gasket on No 1 and No3 bearing caps (p1-28)
oil pan gasket
crankcase gasket
thermostat housing
coolant/water pump
injectors
fuel pump (feed pump assembly) (x2)
injection pump – see

SPECIAL TOOLS

Crankshaft pilot bearing puller	8523-1807
Valve spring replacer	8523-1423
Valve guide replacer	8523-1212

Pulley pull (sized to remove crankshaft pulley)
Valve lapper with suction cup (sized to remove these valves)

SEALS
Crankshaft front oil seals
Crankshaft rear oil seal

PISTON RINGS
Oil ring

OTHER ITEMS
Adhesive KE 42RTV
Belcobond No 4 - Silicone rubber base adhesive

Overhaul checklist

Is the engine doing any of the following?

Cylinder compression Less than 284 psi indicates need for service
1) Allow engine coolant to reach 75 oC
2) Remove nozzles and insert compression tester
3) Cranking the engine (at 250 rpm) with the intake shutter wide open
4) Compression pressure in EACH cylinder should be more than 284 psi (20 kg/cm3

Check oil consumption
1) Assuming oil mileage (or hours/1tr) of a new engine to be as 100%, engine due for overhaul when oil mileage (or hours/1tr) has declined to 60%.

Increase in fuel consumption per hour
1) Assuming fuel mileage (or hours/1tr) of a new engine to be as 100%, engine due for overhaul when fuel mileage (or hours/1tr) has declined to 60%.

Noises
1) Check for abnormal operating noises
2) Knocking
3)	examples?

Major Engine Disassembly

Remove engine from boat
Disconnect propeller shaft coupling from transmission
Support transmission underneath

Drain raw water from heat exchanger
Remove alternator belt
Remove raw water pump belt
Disconnect and remove raw water pump and hoses
Detach heat exchanger from bell housing
Remove 1st rubber hose from heat exchanger and catch engine coolant in bucket
Remove 2nd coolant hose from heat exchanger and catch engine coolant in bucket
Remove heat exchanger – check anode and flush
Remove both rubber coolant hoses from engine

Unbolt exhaust manifold from exhaust pipe

Remove throttle cable support from bell housing
Remove gear cable from transmission
Unbolt bell housing (with the transmission attached) and remove
Disconnect fuel line (and close hose end with bung)
Disconnect return fuel line (and close hose end with bung)
AT BATTERY - disconnect RED Starter wire
Disconnect all engine sensor wiring, incl. block BLACK ground wire

Secure hoist to BOTH lift points on top of engine
Remove engine from boat

Workshop disassembly

Drain crankcase oil
1) Drain crankcase oil and cooking system prior to disassembly
2) Remove oil dipstick

Remove secondary fuel filter
1) Disconnect fuel pipe at joint on secondary fuel filter and on the injection pipe
2) Remove bolts attaching fuel filter and remove the fuel filter assembly

Remove fuel lines
1) Disconnect injector pipes
2) Disconnect leak-off/return pipe from the nozzle holders/injectors

Remove oil filter
1) Remove oil filter and oil filter assembly
2) Disconnect the rocker arm shaft oil feed pipe

Remove timing gear case
1) Remove bolts attaching the timing gear case.
2) Remove the injection pump assembly.
3) Cover injection pump to prevent dirt from entering the delivery valve holder.

Remove injectors
1) Remove the injection nozzle holders.

Remove oil pressure indicator switch
1) Unscrew oil pressure indicator switch (located under injection pump assembly).
2) Unscrew second oil pressure sender (located under injection pump assembly).

Remove alternator
1) Disconnect RED wire to Starter/Battery.
2) Disconnect Smart Regulator wires.
3) Disconnect BLACK ground wire.
4) Slacken and remove alternator belt.
5) Remove alternator and alternator bracket and bolts.

Remove starter
1) AT BATTERY - disconnect RED wire to starter.
2) Unbolt and remove starter.

Remove water pump/engine coolant pump
1) Remove bolts securing water pump/engine coolant pump.
2) Remove complete assembly.

Remove crankshaft pulley
1) Flatten out the bolt lock washer on the crankcase pulley.
2) Remove crankshaft pulley with a pulley pull.
Remove timing gear case
1)	remove timing gear case cover.
2)	remove idle gear.

Remove cylinder head
1) Remove cylinder head cover (valve cover).
2) Unbolt rocker arm shaft assembly - loosen bolts evenly in progression.
3) Pull out the pushrods – number by cylinder number.
4) Unbolt cylinder head bolts – loosen bolts evenly in 3 steps in progression
IN REVERSE ORDER FROM DRAWING (ie. Outside to inside).

5) Remove cylinder head.
6) Remove cylinder head gasket.

Remove crankcase
1) Unbolt crankcase, and remove together with the oil pan (sump).
2) If stuck to block, pry off with a screw driver in the grooves in the crankcase).

Remove oil pump
1) Disconnect the pipe at the joint on the side of the cylinder body.
2) Unbolt and remove the oil pump from the side of the cylinder body.

Remove camshaft thrust plate
1) Unbolt camshaft thrust plate
2) Remove the camshaft – with extra care not to scratch camshaft bearings.

Remove engine thrust plate
1) how?

Remove valve tappets
1) Use valve lapper with suction head to remove tappets from the oil pan side.
- number by cylinder number.

Remove pistons and connecting rods
1) Remove connecting rod bearing caps – number by cylinder number.
2) Clean any carbon from upper part of cylinder wall.
3) Push out each piston with its connecting rod towards the cylinder head side.

Remove flywheel
1) Unbolt and remove damper plate/drive plate.
2) Flatten out 3 lock plates.
3) Remove the flywheel mounting bolts – in diagonal sequence.
4) Remove flywheel.

Remove flywheel housing
1) Unbolt and remove flywheel housing.

Remove crankshaft
1) Remove crankshaft bearing cap bolts – loosen in 3 steps in progression.
2) Handle REAR bearing cap with CARE – it is fitted with lipped oil seal.
3) Number bearing caps by cylinder number. DO NOT interchange.
4) Remove crankshaft pilot bearing with special crankshaft bearing puller.

5) Remove crankshaft bearings and bearing caps.
6) Remove the thrust bearings – number by cylinder number.
7) Remove the crankshaft.

Rocker Arm & Shaft (Layshaft) Assembly
Cylinder Head Assembly
Combustion Chambers
Valves & Valve Guides
clearances
valve seats
valve head
valve springs
Pushrods & Tappets
Hot plugs
Cylinder Body
Piston & Piston Ring Assemblies
pistons
piston rings
ring gap
ring clearance

Exhaust Manifold Assembly

Inspection and Reassembly of Major Engine Parts

General Precautions
1) Wash disassembled parts clean to remove dust, carbon, oil, grease, rust or scales before inspection, correction and adjustment. SPECIAL CARE with aluminum alloy parts to avoid scratching.
2) Apply a cylinder number mark to the valves, bearings, pistons, connecting- rods and all other parts of selective combinations to avoid interchanging them.
2) Examine the cylinder body and cylinder head for damage.

Oil ports
1) Clean oil ports with compressed gas
2) Verify all ports are free from restrictions

Disassembly of Rocker and Shaft (Layshaft) Assembly
1) Remove the snap ring from each end of the rocker arm shaft.
2) Remove the springs, rocker arms, rocker arm shaft brackets and rocker arm shaft.
3) Keep separate rocker arms from each cylinder to prevent interchanging.

Reassemble these parts in the reverse order of disassembly.

Inspection
1) Measure the outside diameter of the rocker arm shaft with an outside micrometer.
2) Replace the rocker arm shaft if the measured value is beyond the limit:

Rocker Arm Shaft Diameter
Normal diameter	19.00 mm
Limit for use	18.85 mm

3) Measure the inside diameter of the bushings with an inside micrometer.
4) Replace the bushings if the measured values are beyond the limit:

Clearance rocker arm shaft/bushing
Standard clearance	0.01 – 0.05 mm
Limit for use	0.2 mm

5) Check the faces of the rocker arms in contact with the value stem end for wear.
6) Replace the rocker arms if the amount of wear is considerable.
7) Remove slight scores (or wear) on the curved face of the rocker arm with an oil stone or grinder.

Cylinder Head Assembly

Disassembly

Remove Glow Plugs
1) Disconnect wire from glow plug connector blade.
2) Unscrew glow plugs and remove from the engine.
3) Test each glow plug (see pXX).

Remove Valve Springs
1) Compress each valve spring with the valve spring compressor.
2) Remove the split collar, the valve spring and the valve.
3) Keep all items from each cylinder together. Do not interchange.
4) Remove the valve stem seal from the valve guides.
5) Drive the valve guides out toward the lower face of the cylinder head, using special tool – valve guide replacer.

Remove Injector Head Shields
1) Insert a rod (5 – 7 mm) into the nozzle/injector hole in the cylinder head.
2) Hold rod so that it is resting against the upper edge of the threaded injector hole.
3) Drive out the hot plug (at the bottom of the swirl chamber) with a hammer and the rod. Be careful not to damage the heat shield.

Cylinder Head Inspection
1) Carefully remove carbon from the lower face of the cylinder head.
2) Be especially careful NOT to scratch the valve seat faces.

Examine the entire cylinder head for cracks or damage
1) Use a magnetic flaw detector or red check, as needed.
2) Test for water leaks with hydraulic tester using 71 psi (5 kg/cm2) for 3 minutes.

Inspect lower face of cylinder head for distortion
1) Check in 6 directions using a straightedge and a feeler gauge.
2) Distortion over 0.2 mm, correct with a grinder, so that maximum distortion is held within 0.05 mm.

Inspect joining face of manifolds for distortion
1) Use a magnetic flaw detector or red check, as needed.
2) Test for water leaks with hydraulic tester using 71 psi (5 kg/cm2) for 3 minutes.
3) Check in 6 directions using a straightedge and a feeler gauge.
4) Distortion over 0.4 mm, correct with a grinder, so that maximum distortion is held within 0.05 mm.

Combustion Chambers Inspection
1) Carefully remove carbon from the combustion chambers to prevent scratching of the hot plug fitting faces.
2) Check the heat shield and hot plug fitting holes in the combustion chamber for damage.
3) Check the hot plug fitting faces for cracks and damage. Replace the cylinder head assembly if any abnormal condition is noticeable.
4) High spots or burrs on the hot plug could cause poor seating of the hot plug.

Valves and Valve Guide Inspection

1) Check the looseness of valve stem in the valve guide to estimate the amount of wear in the valve guide.
2) Using outside micrometer, measure outside of the valve stem in THREE places.

Valve Stem OD	Intake	Exhaust
Nominal diameter	8 mm	8 mm
Limit for use	7.88 mm	7.85 mm

3) Using inside micrometer, measure inside of the valve guide in THREE places.
4) Subtract ID from stem OD. If clearance between valve stem and the valve guide is more than 0.25 mm, replace both parts, or either one that has higher rate of wear.

Valve Guide Clearance	Intake	Exhaust
Nominal diameter	0.039 – 0.068 mm	0.064 – 0.093 mm
Need for service	0.18 mm	0.25 mm

Valve Seats Inspection
1) Check the valve seats for abnormal contact or damage. Correct or replace if found to be at fault.
2) Before correcting the valve seat, check the valve guide and replace with new one if found to be worn as normal condition of the valve guide is essential to obtain the correct valve seat angle.
3) Cut the valve seat using seat cutters of 150, 450 and 750 so that standard contact width is obtained.

4) When cutting the valve seat use a guide rod selected according to the valve guide diameter.
5) Measure valve seat contact width.

Valve Seat Contact Width	Intake	Exhaust
standard	1.2 – 1.5 mm	1.2 – 1.5 mm
need for service	> 2 mm	> 2 mm

6) Measure valve seat depression.

Valve Seat Depression
Normal depression	3.1 mm
Need for service	3.6 mm

7) If amount of valve seat depression is beyond valve of need for service, replace the valve seat insert.

Valve Seat Insert Procedure
1) With an oxy-acetylene cutting and welding torch heat opposed 2 portions of the valve seat insert inner face until red hot (700 – 8000C)
2) Allow the valve seat insert to cool from 3 to 5 minutes, so that contraction of the valve seat insert takes occurs.
3) Pry off the valve seat insert using a screwdriver.

4) Remove carbon and oxidized metal from valve seat insert bores in the cylinder head.
5) Measure the diameter of the valve seat insert bores and select the valve seat inserts according to the following table:

Valve Seat Inserts	Grade	Insert bore diameter	Insert OD
Intake valve	A	40.00 – 40.03 mm	40.11 – 40.13 mm
	B	40.031 – 40.05 mm	40.131 – 40.16 mm
Exhaust valve	A	34.00 – 34.03 mm	34.11 – 34.13 mm
	B	34.031 – 34.05 mm	34.131 – 34.16 mm

6) Press the valve seat insert all the way into the bottom of the valve seat insert bore. Then, lap the seating face.

7) Check the head and stem of the intake and exhaust valves for wear, burning and distortion; replace as necessary.
8) Also check the replace the valves if the thickness of the valve head is less than the limit.

Thickness of Valve Head
Standard	1.3 mm
Limit for Use	1.0 mm

9) Correct the seating face of the valves to an angle of 450, using a valve grinder. Correct the valve stem end as necessary.
10) Apply valve lapping compound to the seating face of the valve and lap the valve seat, using a valve lapper with a section head.

11) When the valve lapping is completed, check that valve contact width is within the specified range and contact is well centred on the valve seat.
12) Too wide a contact width will permit carbon to become lodged between valve and seat while too narrow a contact width accelerates wear of the parts.

Valve Spring Inspection
1) Visually check the valve springs for damage.
2) Position the valve spring on a surface plate. Using a square, check amount of deviation of the valve spring from vertical.

Vertical Deviation of Valve Spring
Limit for use	1.5 mm

3) Check tension of the valve springs with a spring tester. Replace springs if measured value is beyond the limit for use.

Valve Spring under Tension	Free length	Spring tension (set length 39 mm)
Standard	46 mm	18.5 ± 1 mm
Limit for Use	44.5 mm	17.9 mm

Push-Rod and Tappets Inspection
1) Check the push-rods for wear or bending using a feeling gauge.
2) Replace if amount of wear or bending is considerable.

3) Check the face of the tappets in contact with the push-rod for wear or scores. Replace, if defective.

4) Measure OD of tappets with an outside micrometer. Replace if amount of reduction in OD is beyond the limit.

Reduction in Tappet Diameter
Nominal diameter	13 ø
Limit for use	12.95 ø

Clearance Between Tappet & Cylinder Body
Standard	0.1 – 0.4 mm
Limit for Use	0.1 mm

Installation of Hot Plugs
1) Align the ball of the hot plug with corresponding groove in the cylinder head and install the hot plug in position by tapping the circumference of the hot plug lightly with a copper hammer.
2) Hold a soft metal plate with smooth surface on the hot plug to protect the face of the hot plug against damage.
3) Press the hot plug into position by gradually applying a maximum pressure of 4 tons. Avoid the use of extreme pressure.
4) When a new hot plug is installed, grind the end of the hot plug flush with the cylinder head face using a surface grinder.

Maximum Allowable Depression of Hot Plugs	0.02 mm

Valve System Reassembly
1) Drive the valve guide into position from the upper face of the cylinder head, using special tool (valve guide replacer).

Valve guide position above cylinder head	Intake	Exhaust
	13 mm	14 mm

2) Install the oil seal on each valve guide. Be careful to avoid distortion.
3) Install the valve springs and valve spring seats.
4) Compress the valve springs with the aid of a valve spring compressor.
5) Install the split collar.
6) Install the manifold gasket and manifold assembly.
7) Install the glow plugs and connect the wiring connector.

Cylinder Body

Cylinder Body – inspection for cracks
1) Check the cylinder body for cracks.
2) Make water test, in the same manner as used to check cylinder head.

Distortion of Cylinder Body Upper Assembly
Standard	< 0.05 mm
Need for service	< 0.2 mm

Correction of Cylinder Bores

Standard cylinder bore	86 mm

1) With a cylinder bore gauge, measure the cylinder bore at upper, middle and lower portions of the cylinder in two directions:
1) in line with axis of the crankshaft
2) at right angles to the axis of the crankshaft
2) Rebore cylinders if amount of wear is beyond the standard value, cylinder wall is scuffed or it has a trace of piston seizure.
3) When measurements are taken, determine piston oversize according to the largest bore diameter. Using an outside micrometer, measure outside diameter of the pistons at the skirt, in the direction of the side thrust (ie. away from wrist pins), at normal room temperature (200C).
Oversize pistons are available in 6 different sizes:
(mm) 0.25, 0.50, 0.75, 1.00, 1.25, 1.50
4) Calculate the bore diameter to be obtained AFTER honing using the following formula: Cylinder bore after honing = P + C – H ± E
P – piston outside diameter	H – allowance for honing
C – piston clearance	E – error in boring finish

Purpose of honing is to remove traces of the cutting tool used in boring, thereby smoothing the cylinder bore. Amount of material removed from the cylinder wall during honing should be kept to minimum, or finishing accuracy of the cylinder bore will be adversely affected.
5) Measure cylinder bore after honing completed.
6) Cylinder bores should ALL be of a uniform size. Maximum variation 0.02 mm.

Piston and Piston Ring Assemblies

The engine is equipped with aluminum alloy pistons, each having three compression rings and one oil control ring.

Cylinder bores are not equipped with sleeves.

Disassembly
1) Remove the piston rings from the piston, using a piston ring expander.
2) Keep piston rings separate, each set to their own cylinder.
3) Remove piston pin snap rings, using snap ring pliers.
4) Heat piston to 50 – 600C, using piston heater, and remove the piston pin.
5) Keep rings, piston, pin and connecting rod in separate groups in the order of cylinder number.
6) Pistons have a mark on top indicating the front side of the piston.
7) When re-installing the piston and rod units, ensure the mark is toward the front of the engine and that the side of the rod stamped with the cylinder number is towards the camshaft side of the engine.

Piston Inspection
1) Visually check the pistons for scuffs, cracks or traces of seizure and replace if defective.
2) Measure outside diameter of piston skirt, at 900 to piston pin hole, using outside micrometer.
3) Measure cylinder bore diameter at skirt height, using cylinder bore gauge.
4) Compare these two measurements, to determine piston clearance.

Piston Clearance
Standard	0.104 – 0.124 mm at 200C

5) Alternate method:
a) Insert feeler gauge of standard spec. Thickness between cylinder wall and piston.
b) Push piston against opposite side of cylinder.
c) Pull the feeler gauge with a pull scale and note reading on the scale.
d) Normal is 0.5 – 1.0 kg pull on each cylinder.

Piston Rings Inspection
1) Replace piston rings if found to be worn or broken, or if cylinder have been rebored.
2) Ring Gap Inspection:
a) Insert piston ring into the cylinder (without piston) and push down until it is 900 to cylinder wall.
b) Check gap with feeler gauge.

Piston Ring Gaps	1, 2, 3 compression rings	1 and 2 oil rings
Standard	0.2 – 0.4 mm	0.1 – 0.3 mm
Limit for use	1.5 mm	1.0 mm

3) When installing new piston rings on pistons without reboring cylinders, measure the piston ring gaps with the piston rings held at the lower portion of the cylinder (where bore diameter is generally smaller due to less wear).

Piston Ring Clearance Inspection
1) Measure the clearance between the piston ring and the ring groove in each piston, using a feeler gauge.
2) Take measurements at several points around the circumference of the piston.

Piston Ring Clearance	Standard	Limit for Us
1st & 2nd compression rings	0.045 – 0.075 mm	0.3 mm
3rd compression ring	0.030 – 0.060 mm	0.3 mm
1st & 2nd oil rings	0.020 – 0.054 mm	0.15 mm

Piston and Connecting Rod Reassembly
1) Heat piston to 70 – 1000C.
2) Align side of the connecting rod with the cylinder number mark is turned towards the camshaft side.
3) Align small end hole of connecting rod with the piston pin hole and install the piston pin.
4) Normal clearance between the piston pin and connecting rod small end bushing allows piston pin to be press-fitted by hand at normal room temperature after lubricating with engine oil.
5) Replace either the piston pin or the bushing if the pin fits loosely into the bushing.

Piston Pin	Standard	Limit for Use
& Small End Clearance	0.008 – 0.020 mm	< 0.0.05 mm

6) Install piston pin snap rings.
7) Install piston rings in correct order, using piston ring expander:
a) N mark upwards.
b) 1st compression ring is chamfered.
c) Install 3rd compression ring with undercut side down.
d) Install the 1st oil ring on the piston with the expander ring.

8) NOTE: Pistons have a mark on top indicating the front side of the piston.
9) When re-installing the piston and rod units, ensure the mark is toward the front of the engine and that the side of the rod stamped with the cylinder number is towards the camshaft side of the engine.

Connecting Rods
1) Check rods for bending, distortion and/or damage.
2) Check for alignment and parallelism between the big-end and the small-end, using connecting rod aligners.
3) If beyond service limit, correct or replace connecting rod.

Connecting Rod Alignment	Distortion	Misalignment
Standard per 10 cm length	< 0.08 mm	< 0.05 mm
Need for Service	> 0.2 mm	> 0.15 mm

4)	Assemble the connecting rod to the crankshaft and measure the side clearance between the connecting rod big end and the crankpin, using a feeler gauge.
5) Replace the connecting rod if clearance is beyond limit for use.

Big End – Crankpin Clearance
Standard	0.18 - 0.30 mm
Limit for Use	> 0.35 mm

6) When fitting a new bushing into the connecting rod small-end, finish the inner face with a reamer, according to the piston pin diameter.
7) Check weight of assembled piston/connecting rods between each cylinder. Should be within 15 grams. If not grind, or select parts to equalize weight.

Connecting Rod Bearings
1) Check the connecting rod bearings for wear, poor contact, traces of seizure or loss of tension. Replace if found to be defective.
2) Install the connecting rod bearing and bearing cap and tighten.

Bearing cap torque	8 m-kg

3) Measure inside diameter of the bearing with an inside micrometer.
4) To measure oil clearance:
a) Wipe bearings clean and crankpins to remove dust and oil.
b) Use plastigauge in the direction of the axis of the crankshaft, in position away from the oil port in the bearing.
c) Install the connecting rod bearing cap and tighten the bearing cap bolts to the specified torque (see above).
d) Do not rotate or move the crankshaft or connecting rod with plastigauge installed.
e) Remove bearing cap bolts and bearing cap.
f) Measure plastigauge against the printed scale.

Connecting Rod Bearing Oil Clearance
Standard	0.029 – 0.082 mm
Limit for Use	> 0.12 mm

5) Never file the bearing caps or scrape the bearings or install skims in attempt to adjust oil clearance.
6) If the oil clearance has increased due to wear in the crankpins or bearings, have the crankpins ground and install undersized connecting rod bearings.

7) When installing undersize connecting rod bearings, have crankpins ground to size indicated below:

Connecting Rod Bearing Size	OD crankpin after grinding
standard	53.00 ø – 0.070 / - 0.082
Undersize 0.25	52.75 ø – 0.070 / - 0.082
Undersize 0.50	52.50 ø – 0.070 / - 0.082
Undersize 0.75	52.25 ø – 0.070 / - 0.082
Undersize 1.00	52.00 ø – 0.070 / - 0.082

P1-24

Crankshaft bearings
1) The crankshaft is supported on four main bearings.
2) The crankshaft bearings should be inspected and replaced in the same manner as used for connecting rod bearing inspection.
3) Main bearings are renewable precision insert type, with crankshaft end play controlled by thrust inserts located in the cylinder block on the rear intermediate bearing.
4) Bearing inserts are available in standard and undersizes.

Crankshaft Bearing Oil Clearance
Standard	0.019 – 0.064 mm
Need for Service	> 0.12 mm

2) When installing undersize crankshaft bearings, have the crankshaft journals round to the size indicated below:

Crankshaft Bearing Size	OD of crankpin after grinding
standard	70.00 ø – 0.068 / - 0.080
Undersize 0.25	69.75 ø – 0.068 / - 0.080
Undersize 0.50	69.50 ø – 0.068 / - 0.080
Undersize 0.75	69.25 ø – 0.068 / - 0.080
Undersize 1.00	69.00 ø – 0.068 / - 0.080

 Crankshaft
1) Visually check the crank journals, crankpins and oil seal fittings faces for scores or wear, and oil ports for clogging.
2) Measure the outside diameter of the crankpin journals and crankpins, using an outside micrometer.
3) Take measurements at several places on the crank journals and crankpins to determine, 1) amount of uneven wear, 2) out-of-round.
4) If the amount of uneven wear or out-of-round is more than 0.05 mm, have the crank journals and crankpins ground to size indicated in the table and install undersize bearings.

Crankpins & Crank Journals
Nominal dia. of crank journals	70 ø
Nominal dia. of crankpins	53 ø
Crank journal & crankpin finishing accuracy	> 0.007 mm

5) Check crankshaft for run-out. Correct if amount is above Need for Service.

Crankshaft Run-out
Standard	< 0.03 mm
Need for Service	> 0.06 mm

6) To check crankshaft run-out:
a) Support crankshaft on V blocks at its outermost journals
b) Hold the probe of the dial indicator in contact with the centre journal.
c) Note reading on the dial indicator while slowly turning the crankshaft one full turn.
d) Note: HALF the dial reading indicates the actual crankshaft run-out.
7) Inspect the crankshaft thrust clearance.
8) Install the thrust bearing so that the side with the oil groove is turned to the crankshaft thrust face.
9) Check at the clearance at the centre bearing, using a feeler gauge.

Crankshaft Thrust Clearance
Standard	0.04 – 0.198 mm
Need for Service	> 0.30 mm

10) Install oversize thrust bearing if measured value is beyond the limit.

Crankshaft Oil Seals

Front Seal
1) To renew the crankshaft front seal:
2) Remove the timing gear cover.
3) Install the new seal with the lip inward (to the rear) using a suitable seal driver.
4) Lubricate the lip of the seal and crankshaft pulley seal contact area before reassembly.

Rear oil seal
1) To renew the crankshaft rear oil seal:
2) Remove the flywheel and the engine rear plate.
3) The oil seal can then be removed from the rear of the cylinder block and the main bearing cap.
4) Apply a thin coat of liquid Silicon gasket material to the outer circumference of the new seal.
5) Lubricate the seal lip and crankshaft oil seal surface.
6) Using a suitable driver, install the new seal.

Crankshaft Installation
1) Coat thrust bearings with grease.
2) Stick thrust bearing into position at rear intermediate main bearing.
3) Be sure thrust bearings are installed with bearing metal surface (oil groove side) toward the thrust side of the crankshaft.
4) Apply a light coat of liquid silicone gasket material to the side surfaces of the front and rear bearing caps.
5) Apply a light coat of liquid silicone gasket material to the back side of the oil pan packing (arch seals).

6) Apply a small amount of liquid silicone gasket material to the outside diameter of the crankshaft rear oil seal.
7) Apply grease to the seal lip and place the seal on the rear end of the crankshaft with the lip to the inside (forward).
8) Place the upper bearing inserts in the cylinder block.
9) Lubricate the bearings and crankshaft journals.
10) Lower the crankshaft squarely into the block.
11) Take care not to dislodge the thrust bearings.
12) Make sure that the rear oil seal is in its proper position.
13) Place the lower main bearing inserts in the main bearing caps.
14) Install the caps and tighten evenly.

Main bearing cap torque	116 – 130 ft/lbs

Flywheel and Ring Gear
1) Check the face of the flywheel in contact with the clutch driven plate for wear and warpage.
2) Measure warpage in the driven plate with a dial indicator. Replace if measured value is more than 0.1 mm.
3) Visually check the ring gear for wear and/or damage. (Toothed gear that connects to starter motor)
4) If wear in the ring gear teeth is localized to a certain area, the ring gear can be removed, rotated 900 and reinstalled.
5) The ring gear is thermally fitted to the flywheel. It can be removed or installed from or to the flywheel by heating the ring gear with a gas burner.

Camshaft
1) Visually check the camshaft journals, cam lobes and oil pump drive gear for wear and/or damage.
2) Measure height of the cam lobes, using an outside micrometer.
3) Replace the camshaft if the amount of reduction in the height of the cam lobes is beyond the limit for use or if the cam faces are found to be badly scored.
Slight scores on the cam faces may be removed by using an oil stone.

Cam Lobe Height
Standard	40.6 mm
Limit for Use	40.2 mm

4) Measure the diameter of the camshaft journals, using an outside micrometer.
5) Replace the camshaft if the amount of wear is beyond the limit for service.

Diameter of Camshaft Journals
Standard	48 mm
Limit for Use	47.6 mm

6) Measure the camshaft end play with a feeler gauge.
a) install the gear on the camshaft.
b) push the thrust plate against the cam gear.
c) measure the clearance between the thrust plate and the journal.
7) Replace the thrust plate if measured value is beyond limit for service.

Camshaft End Play
Standard	0.050 mm
Limit for Use	> 0.2 mm

Timing Gears
1) Visually check the timing gears for wear and damage.
2) Replace the timing gears if found to be defective.
3) Measure the backlash between the timing gears, using a feeler gauge or dial indicator.
4) Replace the timing gears if the amount of backlash is more than 0.3 mm.

Timing Gears Backlash
Standard	0.1 mm
Limit for Use	> 0.3 mm

Camshaft Gear
1) To renew the camshaft gear and/or thrust plate:
2) Remove the gear retaining bolt from the front end of the camshaft and pull the gear off the shaft.
3) Unbolt and remove the thrust plate from the front face of the cylinder block.
4) When re-assembling, lubricate the thrust surfaces.
5) Be sure the timing marks on the camshaft gear are facing outwards.
6) Tighten the camshaft thrust plate.
7) Tighten the cam gear bolt.

Torque specifications
Camshaft thrust plate	51 ft/lbs
Cam gear bolt	80 ft/lbs

Idler gear
1) Check for end play.

Idler Gear End Play
Standard	0.05 – 0.115 mm
Limit for Use	0.2 mm

2) To renew the idler gear bushings, idler gear shaft or the plate:
3) Remove the two plate retaining bolts and gear from the shaft.
4) Remove the shaft from the block.
5) Check the idler gear shaft.

Idler Gear Shaft Diameter
Standard	44.945 – 44.975 mm
Limit for Wear	0.1 mm

6) Be sure the oil hole in the shaft is aligned with the oil hole in the block when installing the idler gear shaft.

7) Check oil clearance between idler gear bushing and shaft.

Oil clearance Idler Gear Bushing & Shaft
Standard	0.025 – 0.085 mm
Limit for Use	0.2 mm

8) If necessary to renew the crankshaft gear, use a suitable pulley to remove the gear from the shaft.
9) Prior to installation, heat the new gear.
10) Be sure the “X” marks on the crankshaft gear and idler gear are aligned.
11) Be sure the “Y” marks on the idler gear and the camshaft gear are aligned.
12) Be sure the “Z” marks on the camshaft gear and the injection pump drive gear are aligned.

Manifold Assembly
1) Check the intake and exhaust manifolds for cracks, corrosion or damage.
2) Correct or replace the manifold as necessary.
3) Check joining faces of the intake and exhaust manifolds for distortions.
4) Replace or correct by grinding if the distortion is beyond limit for service.

Manifold Distortion, intake & exhaust
Standard	0.05 mm
Limit for Use	0.2 mm

Engine Reassembly

Precautions
1) Wash all disassembled parts, paying particular attention to the oil ports, bearings, pistons, cylinders etc..
2) Apply new engine oil to the cylinder walls and working faces of the bearings and pistons.
3) Discard used gaskets and install new ones at the time of reassembly. Use liquid gasket as needed to prevent oil leakage.
4) Carefully note oil clearances and other clearances during reassembly.
5) Tighten bolts to their specified torques and do not overtighten.

Reassembly
1) Install the crankshaft bearing upper, crankshaft and thrust bearings in position in the cylinder body.
2) Thrust bearings should be installed so the oil grove side is turned outward.
3) Apply a thin layer of adhesive (KE42RTV) to the face of #1 and #3 bearing caps in contact with the cylinder body.
4) Install these bearing caps. Install quickly, as the adhesive dries quickly and loses adhesive strength over time.
5) Tighten the bear cap bolts to the specified torques and wipe off excess adhesive.

Bearing Cap Torque	17 ± 1.0 m-kg

6) Check the crankshaft end play, with crankshaft installed.

Crankshaft End Play	0.04 – 0.198 mm

7) Install the arch gasket on #1 and #3 bearing caps.
8) Apply Belcobond #4 adhesive to the inner face of the gasket and insert the gasket evenly into the groove in the bearing cap. Hold it depressed with fingers for about 5 seconds.

Projection of Arch Gasket	0 - 0.05 mm

9) Apply a thin coat of silicone rubber-based adhesive to the outer circumference of the rear oil seal.
10) Fill the clearance between the lips of the oil seal with grease and install the oil seal in position, using a setting tool.

11) Install the rear plate.
12) Mount the flywheel to the crankshaft.
13) Tighten the bolts in a progressive sequence to the specified torque.

Flywheel Bolts Torque	8.5 m-kg

14) Lock the bolts by bend the lock plates.

Pistons and Connecting Rod Assemblies

1) Set the piston ring gaps, before installing the piston and connecting rod assemblies.
a) Set the #2 oil ring to the stopper pin.
b) Adjust the remaining rings so that their gaps are 1800 apart.
2) Oil control ring can be installed either side up.
3) Place the expander in the groove and install the ring with the end gap at 1800	degrees away from the expander ends.
4) Install the 3rd compression ring with the undercut down.
5) Install the 2nd compression ring with the “N” mark up.
6) Install the top compression ring with either side up.
7) Be sure to space the ring end gaps at 900 degrees apart.

8) Apply new engine oil to the cylinder walls and the circumference of the pistons	and piston rings.
9) Assemble the piston and connecting rod together so that the “front” mark on top	of the piston will be towards the front of the engine, and the cylinder	number (stamped on the side of the rod) will be towards the camshaft	side of the engine.
10) Piston pins are retained by snap rings. Piston pins are available in standard size	only.

Piston Pin Diameter
Standard	26.995 – 27.0 mm
Limit for use	26.97 mm

11) Pin fit in piston bore should be a slight interference fit.
12) Heat the piston to about 800 C.
13) Pin should then be a thumb press fit into the piston.

15) The connecting rod is fitted with a renewable piston pin bushing.
16) Install the bushing with the oil hole aligned to the oil hole in the rod and finish	hone bushing to fit pin.

Connecting rod bushing
Desired fit clearance	0.008 – 0.020 mm
Wear limit for use	0.05 mm

14) Connecting rod bearings are of the renewable precision insert type.
Install each piston and connecting rod assembly into its specific cylinder. Use a	piston ring compressor.
17) Install each piston and connecting rod assembly with its side with the cylinder	number faced the camshaft side.
12) Install and tighten connecting rod bearing cap bolts to specified torque.

Bearing Cap Bolt Torque	8.0 ± 0.5 m-kg

13) Check connecting rod end play.
14) After installation and tightening, check crankshaft turns smoothly.

Engine Front Plate
1) Apply adhesive (Belcobond #4) to the face of the engine front plate in contact with	the cylinder body and injection pump.
2) Fix the gasket in place.
3) Install engine front plate.

Tappets
1) Lubricate tappets with new engine oil and install them before installing the camshaft.

Camshaft
1) Install the camshaft.
2) Install the thrust plate on the cylinder body.

Camshaft bolt torque	7 m-kg
Camshaft end play	0.08 mm

Oil Pump
1) Install the oil pump assembly.
2) Connect the oil pipes and securely tighten the oil pipe joints.

Oil Pan
1) Apply a thin layer of adhesive (Belcobond #4) to both sides of the oil pan gasket.	(Not so much that it will extrude when gasket tightened.)
2) Allow adhesive to dry for 10 – 30 minutes.
3) Install the oil pan to the crankcase.

Oil pan bolt torque	0.8 m-kg

Crankcase
1) Apply adhesive (Belcobond #4) to the upper and lower faces of the crankcase.
2) Apply adhesive (Belcobond #4) to #1 and #3 bearing cap arch gaskets.
3) Allow adhesive to dry for 10 – 30 minutes.
4) Mount the crankcase(and oil sump) to the engine block.
5) Semi-tighten 4 bolts around the bearing caps.
6) Tighten crankcase bolts evenly in progression.
7) Retighten the 4 bearing cap bolts.

Crankcase Bolt Torque	2.1 m-kg

Timing Gears
1) Install the idler thrust collar on the idle gear shaft.
2) Install the timing gears so that the marks X and Y are aligned.

Timing Gear Backlash	0.1 mm

Cylinder Head
1) Install the cylinder head gasket.
2) Install the cylinder head.

3) Lubricate cylinder head bolts with new engine oil before installation.
4) Tighten the cylinder head bolts in THREE stages, in progression starting from	the centre.

Cylinder Head Bolt Torque
Stage one	3 – 5 m-kg
Stage two	6.5 m-kg
Stage three	8.0 ± 2.5m-kg

Rocker Arm Shafts
1) Connnect the rocker arm shaft oil fee pipe.
2) Install the pushrods.
3) Install the rocker arm shaft (layshaft) assembly.
4) Tighten rocker arm bolts.

Rocker Arm Shaft Bolt Torque	2.5 m-kg

Valve Clearance
1) Adjust valve clearances. Should be done with the engine cold.

Valve Adjustment	1	3	3
Valve arrangement	I E	E I	I E
Cyl #1 at TDC	X X	X	X
Cyl #1 at BDC	-	X	X

Valve Clearance
Intake	0.45 mm
Exhaust	0.45 mm

Crankshaft Front Oil Seal
1) Fill the clearance between the lips of the oil seal with grease.
2) Install crankshaft front oil seal on the timing gear case.
2) Mount the gear case.

Injection Pump
1) Align the mark Z on the injection pump gear with the mark Z on the camshaft	gear.
2) Install the injection pump and fit in in position with the timing gear case	attaching bolts.
3) Install the cover.

Crankshaft Pulley
1) Apply a thin coat of oil to the oil seal fitting face of the pulley.
2) Mount the crankshaft pulley to the crankshaft and tighten the bolt.
3) Lock the bolt by bending the tab of the washer.

Crankshaft Pulley Bolt Torque	15 m-kg

Injectors
1) Use corrugated washer and nozzle washer when installing. Install so that the side	of the washer with groove is turned upward (nozzle side).
2) Install the injection nozzle holder assemblies with the injection pipe joint side	down.
3) Semi-tighten them only.

.

4) Install the cylinder head cover assembly (rocker cover?).
5) Install the manifold gasket and manifold assembly.
6) Install the rear engine hanger.

Thermostat
1) Install the thermostat and thermostat housing.
2) Fix the thermostat housing and front engine hanger with the bolts.

Water Pump
1) Install the engine's water (coolant) pump assembly and adjust plate.

Fan/alternator pulley
1) Install the fan/alternator belt pulley.
2) Install the alternator mounting bracket.
3) Install the alternator and semi-tighten the bolts.
4) Install the alternator belt.
5) Align belt to the three pulleys.
6) Tighten alternator belt – finger pressure.

Alternator Belt Deflection	± 5 mm

Oil Filter
1) Install O ring on the new oil filter, wipe with new engine oil.
2) Mount to the oil filter assembly, turning clockwise.
3) Tighten 1/4 – 1/2 turn with oil filter wrench.

Secondary Fuel Filter
1) Install secondary, on-engine fuel filter.

Injection Pipes
1) Install injection pipes.
2) Tighten nozzle holder assemblies to specified torque.

Injector Nozzle Assembly Bolt Torque	7.5 m-kg

3) Connect leak-off (return) pipes to the injectors.

Starter Motor
1) Install starter motor.

Lubrication

Description
The engine lubricating system uses a full-flow type oil filter. Oil pumped out from the oil pump is first filtered through the full-flow oil filter, before it is forced to the vital parts of the engine via the oil passage in the cylinder body.
Overflow valve - When the engine speed, or resistance in the oil filter is increased due to clogging of the filter element, the oil pressure on the oil pump side overcomes the tension of the overflow valve spring; the overflow valve is pushed open bypassing oil into the oil port.
Oil filter relief valve - The oil filter relief valve is so designed that when the pressure of oil delivered from the oil pump reaches relief valve opening pressure, the relief valve opens and bypasses are part of the oil directly into the oil pan, thus preventing a buildup of high pressure within the lubricating system.

Engine Oil
Engine oil quality	Series 3 API Spec CD or above
Oil viscosity	> 26.70C (800F) SAE 40
< 26.70C (800F) SAE 30
Oil capacity	4.8 L (5 quarts)
Oil pump type	trochoid type
Oil delivery	>13 L/min
Oil pressure, warm engine	idle	25 – 50 (1.75 – 3.51 kg/cm)
full speed	40 – 60 (2.81 – 4.21 kg/cm)
Pump speed	1000 rpm
Pressure of delivery	4 kg/cm2
Oil temperature	50 0C
Oil filter type	full-flow with paper element
Oil filter relief valve opening pressure	4.2 – 4.7 kg/cm2	(system relief to oil pan)
Oil overflow valve opening pressure	0.8 – 1.2 kg/cm2 (clogged filter)

Oil Pump
Clearance rotor, vane and cover	standard	0.02 – 0.07 mm
need service	0.15 mm
Tip Clearance rotor and vane	standard	0.02 – 0.13 mm
Clearance rotor tips and pump body	standard	0.02 – 0.27 mm
Clearance rotor shaft and pump body	standard	0.04 mm
need service	0.2 mm

Oil pump assembly 22230
Rotor & shaft assembly 22231
Pinion gear 22232
Pin 22233
Cover, oil pump 22234
Bolt M8 1.25x50 (2) 02258
Washer M-8 (6) 02241
Bolt, cover M8 1.25x25 (2) 02253
Lock washer M8 (6) 02242
Oil strainer (1) 22239
Case (1) 22241
Bolt M8 1.25x15 (1) 02251
Bolt M8 1.25x25 (2) 02253
Oil pipe assembly (1) 22245*
    * Isuzu parts numbers

Oil Pump Disassembly

1) Remove the oil pan.
2) Remove the oil pressure tube from pump to cylinder block.
3) Remove the retaining bolt (9).
4) Disconnect the oil pipe (15).
5) Remove the strainer case (10) and pump cover (8).
6) Remove the outer vane and vane (7).
7) Pull out the pin (6) and remove the rotor (5).
8) Remove the rotor shaft (2).

Inspection
1) Visually check the vane, rotor and pinion gear (3) for wear.
2) Replace parts if there is considerable wear.
3) Measure the clearance between the rotor, vane and cover.
4) Place straightedge across the rotor cup and use feeler gauge to measure the gap.

Clearance rotor, vane & housing
Standard	0.02 – 0.07 mm
Need for service	0.15 mm

5) Replace either the rotor or the vane if the measured value is beyond the need for service.

6) Measure the tip clearance between the rotor and the vane, by inserting a feeler gauge between the tips and the vane.

Clearance between rotor tips & vane
Standard	0.02 – 0.13 mm

7) Replace the rotor assembly if the measured value is beyond the standard.

8) Measure the clearance between the vane and the pump body (housing).

Clearance between vane & housing
Standard	0.02 – 0.27 mm

9) Replace the pump assembly if the measured value is beyond the standard.

10) Measure the clearance between the rotor shaft and the pump body.

Clearance between rotor shaft & pump body
Standard	0.04 mm
Need for Service	0.2 mm

11) Replace the parts if the measured value is beyond the limit for service.

Reassembly
1) Complete in reverse order of disassembly.
2) Insert the rotor shaft (2).
3) Install the rotor (5) and insert the pin (6).
4) Insert the pin fixing the pinion.
5) Install the vane (7).
6) Replace the strainer case (10) and pump cover.
7) Reconnect the oil pipe (15).
8) Check that the rotor shaft turns smoothly.

1	Oil filter bracket (1) 22200
2	Lock washer M8 (11) 02242
3	Bolt M8 1.25x20 (2) 02252
4	Oil filter backing plate (1) 22201
5	Gasket (2) 22202
6	Oil filter housing assembly (1) 22203
7	Street “L” 3/8 NPT (1) 02694
8	Bolt M8 1.25x40 (6) 02256
9	Hose Assembly 17” (1) 22211
10	Oil filter (1) 22210
11	Inverted flare 3/8 NPT-1/2 hose (2) 02721
12	Hose assembly 11 3/4” (1) 22212
13	Bolt M8 1.25x50 (2) 02258
14	Oil bypass block assembly (1) 23204
15	O-ring (1) 22205
16	Relief valve (1) 22206
17	Reducer, bushing 3/4 to 3/8 (1) 02719*
18	(not on 40hp)
* Isuzu Pisces parts numbers

Oil Filter

Operation
Oil pumped out from the oil pump is filtered through the filter element before it is forced to the vital parts of the engine.

Pressure Relief Valve
If the oil pressure reaches relief valve opening pressure (ie. becomes too high), the relief valve opens and some of the oil bypassed the engine and is sent back into the engine crankcase.

Relief Valve Opening Pressure	4.3 – 4.7 m-kg

Oil Filter Bypass
If the oil filter element becomes clogged, the overflow valve opens, allowing oil to bypass the filter and flow directly to lubricate the engine parts unfiltered.

Disassembly
1)	Remove the oil filter element.
2)	Disconnect the oil pipes (hoses).
3)	Unbolt the oil filter bracket (filter cover) from the engine.
4)	Remove the relief valve (3).
5)	Remove the overflow valve (4,5,6).

Inspection
1)	The relief valve CANNOT be disassembled.
2)	Visually check the valve for damage or abnormal condition.
3)	To check the relief valve opening pressure:
a) connect a pipe to the oil gallery at a point closest to the oil filter.\
b) check the opening pressure, using a pressure gauge.
4)	Replace if found to be defective.

5)	The overflow valve CANNOT be disassembled.
6)	Visually check the valve for damage or abnormal condition.
7)	Replace if found to be defective.

Reassembly
1)	Reinstall the overflow valve.
2)	Reinstall the relief valve.
3)	Bolt the oil filter bracket to the engine.
4)	Reconnect oil filter pipes (hoses).
5)	Install new oil filter.

Cooling System

1	Water pump assembly (1) 32050
2	Plug, heater 3/8 NPT (1) 32119
3	Bearing assembly (1) 32051
4	Set screw M8 special (1) 02652
5	Lockwasher M8 (1) 02242
6	Retainer ring (1) 32052
7	Seal assembly (1) 32053
8	Impeller (1) 32054
9	Flange (1) 32055
10	Cover, rear (1) 32056
11	Gasket (1) 32057
12	Screw, rear cover (7) 32060
13	Gasket (1) 32058
14	Kit water pump repair (1) 92012
16	Bolt M10 1.25x50 (4) 02784
17	Lockwasher M10 (5) 02342
18	Bolt M10 1.25x50 (1) 02785
19	Lockwasher M10 (1) 02342
20	Tension arm (1) 62715
21	Pulley (1) 32059
22	Bolt M6 1.0x12 (4) 02184
23	Lockwasher M6 (4) 02182
24	V belt (1) 32360*
*Isuzu part numbers
Cooling System

Description
The cooling system is in two parts.
Raw Water - Raw water is drawn into the boat through a seacock, passes through a strainer and through a Jabsco impeller pump, then goes to a heat exchanger mounted over the engine's bellhousing. From there the warmer water goes up to the North Sea exhaust and exits the boat with the engine exhaust.
Coolant System - Coolant in the reservoir on the top of the engine is circulated by the water pump through the engine and through the reciprocal pipes of the heat exchanger where the coolant is cooled before returning to the reservoir.

Coolant System
To facilitate quick normalization of the engine, a thermostat is installed in the coolant system so that coolant does not circulate through the heat exchanger until the coolant reaches 76.50C when the thermostat valve begins to open. This allows pressurized coolant to past through the heat exchanger and water jackets parallel to the cylinders inside the engine.

Coolant System Specifications
Thermostat opening temperature	76.5 ± 1.50C
Thermostat valve lift @ 900C	8.0 mm
Thermostat type	Wax-pellet type with by-pass
Coolant pump – type of seal	Impeller with 6 blades
Pump delivery @3000rpm, 2.5 m head	60 L/min
Type of seal	Mechanical
Pulley diameter	114 mm
Pulley ratio (crankshaft to pump)	1.2

Disassembly
1) Remove from the engine body.
2) Remove the rear cover from the pump body.
3) Loosen the set screw.

4) Remove the fan centre, using a puller.
5) Impeller is cast with iron. Do not attempt to drive it off with a hammer.
6) Remove the shaft and impeller from the pump body, using a bench press.

Inspection
1) Check the disassembled parts for wear, cracks, and damage. Replace, if found to be defective.
2) Check the shaft for bending.
3) Check radial play in the bearing unit.

Bearing Unit Radial Play
Limit for service	> 0.2 mm

Re-assembly
1) Turn the seal unit so that its side with spring is turned to the impeller.
2) Install the thrower and seal unit on the bearing fitting portion of the shaft.
3) Install the shaft into the water pump body from the pulley side, using a bench press.
4) Align the screw hole in the pump body with the bearing outer race setscrew hole.
5) Install the impeller on the shaft, using a bench press.

Clearance between Impeller and Pump Body Face	1 mm

Clearance Impeller and Pump Body
Clearance between outer circumference of impeller and pump body	1.2 – 1.3 mm

6) Install the fan centre, using a bench press.
7) Tighten the setscrew and install the rear cover.
8) Check fan centre turns smoothly, when reassembly completed.

Thermostat

1	Housing, lower (1) 32114
2	Housing (1) 32115
3	Thermostat (1) 32118
4	Plug 3/8 NPT (1) 32119
5	Gasket (1) 32120
6	Bolt M8 1.25x30 (2) 02254
7	Lockwasher M8 (2) 02242
8	Temperature Sender (1) 62635
9	Gasket (1) 32122
10	Bolt M8 1.25x25 (4) 02253
11	Lockwasher M8 (4) 02242
12	Flatwasher M8 (4) 02241
13	Hose, bypass (1) 32123
14	Clamp #8 (2) 32391*
*Isuzu Pisces parts numbers

Thermostat specifications
Thermostat opening temperature	76.5 ± 1.50C
Thermostat valve lift @ 900C	8.0 mm
Thermostat type	Wax-pellet type with by-pass

Removal
1) Disconnect the coolant outlet pipe.
2) Remove the thermostat from the thermostat housing.

Inspection
1) Check and replace thermostat if it remains open at normal room temperature.
2) Check valve opening temperature and valve lift by submerging in water and heating the water slowly.
3) Replace the thermostat if measured values deviate from the standard values.
4) Allow sufficient time for valve to open when checking for valve lift or value opening temperature. Reaction of the thermostat is somewhat sluggish. It takes 3 to 5 minutes for the thermostat to respond to the change in temperature.

Installation
1) Use a new gasket.
2) Install the thermostat into the thermostat housing so that the flanged portion of the thermostat is brought into good contact with the upper face of the housing.
3) Install the coolant outlet pipe.

Fuel System

Description
The model 2AB diesel engine is equipped with Bosch K type flange-mounted fuel injection pump. This incorporates an efficient governor for stable engine operation through all ranges of speed.

The PES-A type fuel injection pump for model 3AB and 3AA diesel engines is identical in construction and operation to that for model 2AB and 2AA engines.

Injection Pump
The plungers are lifted by the cam and lowered by the action of the plunger spring repeatedly to deliver a metered amount of fuel.

Timing
The injection pump should be correctly timed when installed with the “Z” marks on the pump drive gear and the engine camshaft gear are aligned; and when the notches (scribe marks) on the pump housing and mounting flange are aligned.

Some engines may have an inspection hole in the front of the timing cover, so that timing marks may be checked without removing the timing cover.

Adjusting Timing
If timing marks are suspected of being in accurate, or a new fuel injection pump is being installed, check the pump flow timing as follows:

1) Disconnect #1 fuel injection line from the pump.
2) Remove the delivery valve holder, spring and delivery valve.
3) Reinstalled the delivery valve holder.
4) Turn the engine crankshaft in the normal direction (clockwise from the front of the engine) to bring #1 piston up to TDC on the compression stroke while operating the manual primer pump.
5) Stop turning the crankshaft when fuel stops flowing from the #1 pump outlet (beginning of injection).
6) Check the position of the crankshaft pulley timing marks.
7) Beginning of injection should be 18° BTDC.

8) If timing is not correct, loosen the pump mounting bolts and turned the pump housing on the mounting flange to obtain the correct timing.
9) Scribe new alignment marks on the pump housing and the mounting flange, after proper timing is obtained.

Injection Pump Specifications
Fuel injection timing B TDC	180
Firing Order	1 – 3 – 2
Plunger diameter	6.5 ø
Cam lift	7 mm

The pump housing has a fuel reservoir which is communicated with discharge and intake ports in the plunger barrels. When the plunger lowers and uncovers the discharge and intake port in the plunger barrel fuel is sucked into the plunger barrel until the plunger reaches the bottom dead centre.

When the plunger is lifted beyond the import in the plunger barrel (intake port is covered by the plunger) the fuel trapped within the plunger barrel becomes pressurised. As the pressure of fuel within the plunger barrel increases beyond residual pressure in the injection pipe and overcomes the tension in the delivery valve spring, the delivery valve is pushed open, allowing pressurised fuel into the fuel injection pipe.

When the pressure of fuel in the injection pipe increases beyond the tension of the injection nozzle spring (the injector), the needle valve is pushed open and fuel is injected. As the plunger ascends further and the groove in the plunger meets with the intake and discharge port, a fuel passage is formed to return fuel into the fuel reservoir, thereby preventing further delivery of fuel.

Effective Stroke
The ascending stroke of the plunger, from the point at which the intake and discharge port in the plunger barrel is covered with a circumference of the plunger, to the point at which the spiral groove in the plunger meets with the intake and discharge port is called the “effective stroke”. The amount of fuel injected varies with the effective stroke.

Control Rack
The position of the spiral groove (helix) is controlled by the control rack. A T-shaped flange on the lower section of the plunger is fitted into the groove in the control sleeve. The control sleeve has a pinion that is in mesh with the control rack so that the entire plunger is turned by moving the control rack, and thus controlling the amount of fuel injection.

When the plunger moves up and pressure of fuel within the plunger barrel increases beyond the residual pressure in the injection pipe (and overcomes the tension of the delivery valve spring), the delivery valve is pushed open allowing pressurized fuel into the injection pipe.

As the plunger moves further up and the spiral groove (helix) in the plunger meets with the intake and discharge port in the plunger barrel, delivery of fuel stops; and the delivery valve is closed by the action of the delivery valve spring.

To prevent dripping of the nozzle and counterflow of fuel after injection, the delivery valve has a piston that travels within the stroke to suck in fuel remaining within the injection pipe (see Left side of the illustration above).

Governor

The fuel injection pump is equipped with an RSV type governor which is mainly used for generators and construction machinery which is generally operated under varying load conditions.

The RSV type governor is a mechanical all-speed governor with a device for changing range of speed control and speed variation characteristics.

The Governor is integrated with the pump housing. A pair of flyweights are installed on the end of the camshaft; and a sleeve with sliding away arranged on the camshaft and is held in contact with the flyweight rollers.

Movement of the flyweights is relayed, via the shifter, guide lever and floating lever, to the control rack. The main spring which regulates movement of the flyweights is hooked to the tension lever and swivel lever, so that its tension is controlled by varying the inclination angle of the control lever. An idling spring is hooked to the lower end of the tension lever.

The guide lever is pivoted to a fulcrum pin and a roller is held in contact with the sleeve. The upper end of the guide lever is supported by the pin press-fitted to the control rack which is pushed by the start spring in direction of fuel increase.

The tension lever is pivotally supported by the same fulcrum pin and a governor at spring is hooked to the upper end of the tension lever. The tilting angle of the tension lever is regulated by means of the full-load stopper bolt.

One end of the governor spring is hooked to the arm which is connected, via the control lever shaft, to the control lever. Re-movement of the control lever is regulated by the maximum speed stopper bolt thereby controlling the governor spring tension.

To hold the engine idling speed constant, the idling spring installed in the governor cover works when the control rack is pulled in toward the governor.

NOTE:	Do not attempt to disassemble the governor assembly needlessly, as it is factory-adjusted to suit the engine.

Disassembly
NOTE: Do not attempt to disassemble the governor assembly needlessly, as it is factory-adjusted to suit the engine.
1) Disassembly (and reassembly) requires the use of special tools.

Governor Special Tools Required	DieselKiKi code numbers
Special tool	5790-101
Tappet insert	57921-252
Tappet clamp	57931-602
Tappet holder	57931-200
Socket wrench	57914-150
Fitting plate	57931-002
Bearing inner race extractor - drive side	57925-592
Bearing inner race extractor – governor side	57925-612

2) Prior to disassembly, wash clean the injector pump, being careful to prevent entry of any dirt or foreign matter into the pump.
3) Keep parts removed from each barrel together, and separate, to prevent interchanging.

Injector Pump
1) Remove the drive gear and bracket from the injection pump.
2) Clamp the fitting plate (special tool) securely in a vise and mount the pump on the fitting plate with three bolts. (ie. Pump is held securely in the fitting plate which is held securely in the vise).
3) Remove the bolts fixing the cover plate.
4) Remove the drain bolt and drain the lubricating oil.
5) Raise the tappets by turning the camshaft and keep them apart from the cam by inserting tappet holder (special tool) into the clearance between the tappet adjusting bolt and nut.

Governor Cover
1) Remove the idling spring assembly.
2) Remove 8 bolts attaching the governor cover and remove the cover.
3) Remove the start spring and spring seat.

Flyweight Removal
1) Hold the camshaft from turning at the drive side.
2) Remove the flyweight round nut, using a socket wrench.
3) Remove the flyweights, sleeve and shim, using an extractor.

Full-load Stopper Removal
1) Loosen the full-load stopper bolt adjusting nut.
2) Take out the full-load adjusting stopper bolt from the governor.
3) Remove the closing cover.
4) Remove the angleich spring nut.
5) Remove the idling sub spring.

Tension Lever Removal
1) Remove the screw plug and shaft.
2) Pull out the guide lever together with the roller.
3) Disconnect the tension lever from the governor spring.

Control Lever Assembly Removal
1) Remove the nut connecting the swivel lever with the control lever shaft.
2) Remove the swivel lever shaft, spring washer, shim and governor spring.
3) Drive out the control shaft bushing toward the inside of the cover. Be careful to avoid scratching the shaft.
4) Remove the control lever assembly together with the lever shaft.
5) DO NOT separate the lever shaft from the control lever unless replacing them, because they are connected and adjusted to maintain a proper relationship.
6) Remove the guide lever assembly.
7) Remove the tension lever assembly together with the governor spring.

Inspection of Governor

1) Check the clearance between the guide bushing and shifter. If the clearance is excessive, replace the bushing.
2) Check for play between the shifter pin and guide lever and between shifter pin and floating lever. If the play is excessive, replace either of the parts with higher rate of wear.
3) Check the swivel lever for wear, paying particular attention to the portion supported in the bushing press-fitted to the governor cover. If the amount of wear is excessive, replace either of the bushings or the swivel lever.

4) Springs are to be tested at the time of the governor adjustment.
5) Check the springs for distortion, corrosion or damage and replace if any abnormal condition is noticeable.

Camshaft Removal
1) Remove the bearing cover fixing bolts on the drive side and remove the bearing cover.
2) Withdraw the camshaft toward the drive side exercising care to prevent it from coming into contact with the pump housing.

Tappet Removal
1) Remove the cap from the bottom face of the injection pump.
2) Discard used cap and install a new one at the time of reassembly.
3) Insert a tappet insert (special tool) into the pump housing from the bottom side and clamp the tappet roller.
4) Compress the plunger spring and remove the tappet holder (special tool).
5) Insert the tappet pincers (special tool) into the pump housing from the bearing cover fitting hole and remove the tappet.

Plunger removal
1) Remove the plungers together with the spring seat, using spring pincers.
2) Keep the plungers in clean kerosene.

Pinion Removal
1) Remove the plunger springs and spring seats from the bottom side of the pump housing.
2) Remove the pinion from the cover plate.

Delivery Valve Removal
1) Remove the delivery valve holder lock plate.
2) Remove the delivery valve holder and delivery valve spring, using a socket wrench.
3) Remove the delivery valves with the aid of an extractor.

Plunger Barrel Removal
1) Remove the plunger barrels upward.

Control Rack Removal
1) Remove the control rack guide screw on the rear face of the injection pump.
2) Remove the control rack from the governor side.

Bearing Removal
NOTE: Only remove if replacing them.
1) Remove the bearings fitted onto the camshaft, using an extractor.
2) Extractors – drive side bearing, - governor side bearing.

Adjustment of Governor

Preparation

Installation of Injection Pump
1) Mount the injection pump to the injection pump tester
(Fixing stand PN # 5781-012)

Control Rack Zero (0) Position Setting
1) Remove the control rack cap on the side opposed to the governor and install the measuring device (PN#5782-600) in place.
2) Move the control rack all the way in the direction of fuel STOP.
3) Set ZERO position of the control rack to ZERO position of the measuring device.
4) Apply about 180cc of injection pump oil into the cam chamber and governor chamber of the injection pump. (1 L oil PN#31453-012).
5) Bleed the fuel circuit through the bleeder screws.

Adjustment of Injection Start Timing

Measurement of Plunger Pre-Stroke
1) Check that the control rack is set in position of FULL-LOAD.
2) Bring the plunger in No1 barrel into Bottom Dead Centre and feed pressurized fuel into the injection pump by operating the high pressure control valve on the pump tester.
3) Mount the measuring device (PN#5782-403) to the cover plate window on the injection pump.
4) Hold the contactor of the measuring device in contact with the upper portion of the tappet in the No1 barrel.
5) Calibrate the dial gauge reading to zero.
6) Turn the flywheel in normal direction of rotation until the tappet is lifted 2.1 mm off the Bottom Dead Centre and note the reading of the scale on the flywheel.
7) Remove the measuring device and again lift the plunger from the Bottom Dead Centre by turning the flywheel in normal direction of rotation.
8) Make necessary adjustment by turning in or out tappet adjusting bolt, so that fuel stops flowing out from the overflow valve on the injection nozzle holder when the flywheel is turned to the specified angle. (Double-end wrench PN# 57911-000.)

Measurement of Injection Starting Intervals
1) When the plunger pre-stroke adjustment is completed, make further adjustments on the plunger stroke so that fuel stops flowing out from the overflow valve on the injection pump when the flywheel is turned 2700 30' from the specified point.
2) Still further turn the flywheel 900 30' from this point and check to make certain that fuel stops flowing out from the No1 barrel.

Measurement of Tappet Clearance
1) Bring the tappet in the No1 barrel into Top Dead Centre by turning the flywheel.
2) Further raise the tappet until the upper face of the plunger flange is brought into contact with the lower face of the plunger barrel.
3) Check that lift of the plunger above the Top Dead Centre is more than 0.3 mm.

Adjustment of Injection Volume
1) Measure the amount of fuel injection per plunger stroke, using a measuring cylinder.
2) Measurement should be taken with the control rack fixed and with the pump running at a constant speed because the injection volume rises with varying control rack position and pump speed.
3) To adjust injection volume, proceed as follows:
4) Remove the control rack guide screw on the rear face of the injection pump.
5) Fix the control rack in the specified position with the control rack stopper.
6) Measure the volume of injection with a measuring cylinder by operating the injection pump at the specified speed.
7) Fix the control rack in ZERO position and turn out the screw fastening the pinion to the control sleeve 1/2 of a turn and adjust setting of the control sleeve.
8) This adjustment should be repeated until the specified injection volume is obtained.
9) Injection volume increases when the control sleeve is turned clockwise and decreases when turned counter-clockwise.

Adjustment of Governor

Control Rack Zero Position Setting
1) Tilt the control lever all the way in the direction of the fuel stop, and adjust the position of the control rack to zero.
2) Set the control rack in position of 0.5 – 1.0 mm with the stopper bolt.
3) This adjustment is necessary to protect the linkage against excess load imposed when the control lever is pulled all the way in the direction of the fuel stop.
4) Operate the control lever and check that the full stroke of the control rack is 21 mm.
5) Check that the control rack moves smoothly.
6) If unsmooth, check the injection pump and correct as necessary.

Full-load Stopper Adjustment

1) The full-load stopper is used to control the maximum volume of fuel injection.
2) To adjust, hold the main spring under a slight tension by tilting the control lever and adjust setting of the full-load stopper, so that the control rack is pulled to a position (A mm) when the pump speed is increased to K.
3) The maximum amount of fuel injection increases when the full-load stopper is turned clockwise (as viewed from the governor side), and decreases when the stopper is turned counterclockwise.
4) Hold the control lever in full-load position and adjust setting of the maximum speed stopper, so that the maximum speed stopper begins to work when the pump speed reaches point B.

Swivel Lever Setting Adjustment
1) The lower the speed variation coefficient, the higher the governor efficiency will be. (Speed variation coefficient corresponds to the value obtained by deducting rated speed from the no-load maximum speed.)
2) On a RSV-type governor, the speed variation coefficient can be controlled to a certain extent by adjusting the specific spring constant of the governor spring.

Speed variation = I – L x 100%
    coefficient L

3) Hold the control lever in the full-load position and adjust the setting of the knuckle on the swivel lever, so that the pump speed reaches point G when the control rack is pulled to point H mm.
4) This adjustment will affect tension of the main spring and causes the speed at which the governor starts to work to vary.
5) It is therefore necessary to readjust setting of the maximum speed stopper.

Adjustment of the Idle spring Setting
1) With the engine stationary, set the control lever so that the control rack is held in a position of 9 – 10 mm.
2) Increase the pump speed to C	and check that the control rack is pulled to point B.
3) If the position of the control rack deviates from the specified point, adjust with the idling sub spring.
4) Securely tighten the lock nut once correct adjustment is obtained.
5) Do NOT turn in the idling sub spring excessively, or else the no-load maximum speed will be adjusted too high.

Adjustment of Torque Spring
1) Increase the pump speed to A.
2) Check that the control rack is pulled to point A mm.
3) Gradually increase the pump speed.
4) Adjust tension of the torque spring with the adjusting bolt, so that the control rack is pulled to position B MM when the pump reaches point B.

Injection pump assembly (1) 43201	11	Gasket (2) 42039
1	Delivery Valve (3) 42214	12	Holder (3) 42216
2	Gasket	(3) 42262	13	Dip stick (1) 43207
3	Spring (3) 42215	14	O-ring (1) 42213
4	Oil Seal (1) 42271	15	Bleed screw (2) 42248
5	Cam shaft (1) 43236	16	Hollow bolt (1) 42246
6	Bearing (1) 42237	17	Seal (1) 42271
7	Bearing (1) 42238	18	O-ring (1) 42256
8	Tappet (1) 43220	19	Gear (1) 82322*
9	Plunger (1) 42261	*Isuzu Pisces part numbers
10	Spring (3) 43228

Injection Pump

“The PES-A type fuel injection pump for model 3AB1 (and 3AA) is equal to the injection pump for model C240 and C220 diesel engines. This injection pump is identical in contraction and operation to that for model 2AB and 2AA diesel engines.”

The model 3AB1 (and 3AA) diesel engine is equipped with Bosch A type flange-mounted injection pump.

Fuel injection timing	18
Injecting order	1 – 3 - 2
Plungers	6.5
Cam lift	8

Construction and Operation

Injection Pump Camshaft

The pump camshaft has the combined tangential and eccentric cams with tangential face on the front side.

Tappets
Tappet clearance is adjusted with the adjusting bolt (on top of the tappets).

Reaction Springs
In order to protect the injection pump body against errosive action of the pressurized fuel, a reaction spring is installed in position opposed to the intake and outlet port in the plunger barrels.

Prior to Disassembly
Perform the following check-ups to determine whether or not the injection pump overhaul is necessary.
1) Visually check the injection pump housing for cracks and oil or fuel leakage.
2) Check to see if the camshaft can be turned smoothly by hand.
3) If rotation of the camshaft is unsmooth, the trouble may be due to a defective bearing or plunger spring.
4) Remove the cover plate and check the condition of the plunger springs and control pinions.
5) Check the state of the lubricating oil in the cam chamber to see if fuel is leaking into the cam chamber.

The injection pump is so designed that a slight amount of fuel leads into the clearance between the plungers and plunger barrels to lubricate these parts. However, if the amount of fuel leaking into the cam chamber is excessive, it may be an indication of excessive clearance between the plunger and plunger barrels or between the push-rods and feed pump housing.

6) Operate the control lever and see if the control rack moves smoothly. If the movement of the control rack is unsmooth, it may be due to plunger sticking.

Disassembly
1) Prior to disassembly, wash clean the outside of the injection pump to prevent entry of foreign matter into the pump. Keep parts removed from each barrel separate to prevent interchanging.

Drive Gear Removal
1) Remove the automatic timer in the following manner using extractor (PN#Kiko 57926-581).
2) Screw the boss into the centre hole in the flyweight holder, then turn in the screw rod to depress the end of the injection pump camshaft.

Injection Pump Mounting Bracket Removal
1) Clamp the fitting plate securely in a vise and mount the injection pump to the fitting plate with 4 bolts. (Universal vise PN# 5794-002)
2) Remove the feed pump.
3) Remove the cover plate.
4) Raise and hold the tappets in an elevated position, in the following manner:
5) Bring the tappet to Top Dead Centre by turning the camshaft slowly and insert the tappet holder into the clearance between the tappet adjusting bolt and nut.
6) Remove the bolts fixing the governor cover.
7) Remove the governor cover, in the following way:
8) Pull the governor cover part way out toward the governor.
9) With a screwdriver depress the metal fastener to release the link from the control rack.
10) Disconnect the control rack from the link.
11) Unhook the start spring from the governor housing, using long-nose pliers.

Flyweight Removal
1) With a socket wrench (PN#57915-010) remove the round nut retaining the flyweights.
2) Remove the flyweight assembly from the camshaft by? screwing the extractor (PN#57926-511) into the flyweight holder.
3) Remove the 7 screws fixing the governor housing.
4) Pull out the governor housing from the injection pump housing.
5) Remove the bearing cover and pull out the camshaft toward the pump housing, together with the bearing.
6) Remove the plug screw on the bottom face of the pump housing, using “L” handle (PN#57910-112).

NOTE: Make sure to keep all parts removed from each barrel SEPARATE to ensure reassembly into their original positions. The tappets can be removed easily when the removal operation is performed in sequence of No3, No2, No1 barrels.

Tappets Removal
1) Remove tappets, in the following manner:
2) Insert the tappet holder (PN#57931-210) into the pump housing from the bottom opening and clamp and tappet.
3) Raise the handle on the tappet insert forward and release the tappet holder, then lower the handle.
4) As the handle on the tappet insert is lowered, the tappet is pushed out by the plunger spring.
5) Insert the tappet clamp (PN#57931-621) into the pump housing through the bearing cover fitting hole.
6) Clamp the tappet crosswise and take it out carefully to prevent dropping of the roller pin and injection timing adjusting washer.

Plunger and Plunger Spring Seat Removal
1) Remove that the plungers and plunger spring seats, in the following manner:
2) Insert the plunger insert (PN#57921-562) into the pump housing through the bottom opening and fit it into the hole in the lower spring seat.
3) Pull out the plunger together with the lower spring seat.
4) Keep the plunger and lower spring seat removed from each barrel separate, in clean kerosene to prevent interchanging.
5) Remove the plunger springs through the bottom opening.
6) Remove the upper spring seats through the tappet chamber cover fitting hole.
7) Take out the control sleeve through the tappet chamber cover fitting hole together with the control pinions.

Control Rack Removal
1) Remove the control rack in the following manner:
2) Remove the control rack guide screw on the rear face of the pump body and pull out the control rack towards the governor.

Delivery Valves Removal
1) Remove the delivery valve holder lock plate.
2) Remove the delivery valve holders with socket wrench (PN#57914-050) and ratchet handle.
3) Remove the delivery valve springs and keep them in kerosene.
4) Remove the delivery valve body, in the following manner:
5) Screw the delivery valve extractor (PN#57920-032) onto the outer circumference of the delivery valve body.
6) Hold the extractor guide and depress of the handle so that the delivery valve body is forced out of position.

Plunger Barrel Removal
1) Insert fingers into the pump body through the tappet chamber cover fitting hole.
2) Pull out the plunger barrel. Keep the plunger and plunger barrel from each bore separate and in clean kerosene.

Bearing Inner Race Removal
NOTE: Remove the bearing only when replacing the camshaft or bearing.
1) Remove the bearing inner race with the aid of the bearing in a race extractor (PN#57925-412).

Bearing Outer Race Removal
1) To remove the bearing outer race, proceed as follows:
2) Fit the tapered portions of the bearing outer race extractor (PN#57925-012) into the clearance between the bearing outer race and cover.
3) Turn the nut all the way in and press the knurled end of the bolt with a bench press or tap the end of the bolt with a hammer.
4) Disassembly of the injection pump assembly is completed when all the above steps have been followed.
5) Keep the plungers, delivery of valves together as sets and separate from each other, and in clean kerosene.
Inspection of Injection Pump

Pump Housing
1) Visually check the pump housing for cracks.
2) Visually check the threaded portions for damage.
3) Correct or replace the pump housing as necessary.

Camshafts and Bearings
1) Check the face of the cams for wear or scores.
2) Check the key groove for distortion and/or damage.
3) Replace the camshaft if any abnormal condition is noticeable.

Tappets
The tappet roller assembly consists of roller and roller pin.
Check these parts for wear in the following manner:
1) Hold the probe of a dial indicator in contact with the roller (see below) and screw in or out the adjusting bolt. Note the reading on the dial indicator.
2) Replace both parts if the amount of play is more than 0.2 mm.

3) Check the tappet rollers for wear, scores or separation.
4) Replace the rollers if found to be defective.
5) Check the clearance between the tappets and pump housing.
6) Replace the tappets or pump housing if the measured clearance is:

Clearance between tappet	Standard value for assembly	Limit for Use
and pump housing	0.03 – 0.07 mm	0.2 mm

Control Rack and Pinion
1) Visually check the control rack for bending and team in mash with opinion for wear.
2) Replace the control rack if any abnormal condition is noticeable.
3) Check and replace the parts if amount of backlash between control rack teeth and pinion is in excess of limit for use:

Control Rack Backlash	Standard	Limit for Use
	0.15 mm	0.03 mm

Plungers
1) Wash clean the plungers and check them for scores, discolouration or sticking, paying particular attention to the reed.
2) Replace the plunger assembly if any abnormal condition is noticeable.
3) Wash and clean the plunger assembly.
4) Check operation of the plunger by tilting the plunger assembly about 600 to one side.
5) Repeat the test with the plunger assembly turned a little at a time.
6) Correct or replace the entire plunger assembly if the plunger is binding or if it slides out too fast.

Delivery Valves
1) Check the piston and seat of the delivery valves for scores or damage.
2) Replace the delivery valve assembly if any abnormal condition is noticed.
3) Wash clean the delivery valve assembly.
4) Hold a finger over the opening in the valve seat. Depress the valve lightly.
5) The delivery valve is normal if the valve snaps out when the finger is released.
6) If the valve does not snap out when the finger is removed quickly, replace the valve assembly, as this condition indicates piston wear.

Control Sleeves
1) Measure the width of the groove in the control sleeves.
2) Replace the control sleeve if measured value is more than 7.02 ± 0.08.

Inspection of threads
1) Check threaded portions of the parts and correct or replace parts as necessary.
2) Discard used gasket and O rings. Install new ones when reassembling.

Camshaft
1) Check fit of the key into the key groove for looseness and if necessary, replace either of the key or the camshaft.
2) Check the tapered portion for a regularity. If necessary, remove high spots with an oil stone.
3) Check the threaded portion for damage and correct as necessary.
4) Check the face of the cams for wear or damage. Replace the camshaft if any abnormal condition is noticeable.
5) Check the bearing for wear or damage, and replace the bearing as necessary.
6) Check the camshaft end play in the following manner:
7) Assemble the camshaft to the injection pump and install the bearing cover.
8) Check the camshaft end play with a measuring device.
9) When inspection and adjustment of the camshaft end play is completed, installed the oil seal on the bearing cover.
10) Screw the oil seal guide (57920-870) all the way on to the camshaft and install the bearing cover.
NOTE: This step is important to protect the oil seal against damage in contact with the edges of the key groove or threads on the camshaft when installing the bearing cover.

Adjustment of the camshaft end play
1) If necessary, adjust the camshaft end play to 0.02 – 0.06 mm by means of the shim between the bearing and distance ring.

Camshaft End Play Adjusting Shims
Part number	Thickness (mm)
29311 - 701	0.1
29311 - 702	0.12
29311 - 703	0.14
29311 - 704	0.16
29311 - 705	0.18
29311 - 706	0.5
29311 - 709	0.3

2) Check the screw plug for damage, paying particular attention to wrench sitting groove, and replace as necessary.
3) Check the clearance between the roller and bushing.
4) Check the clearance between the bushing and pain.
5) Replace the tappet assembly if either clearance is excessive.

Clearance tappet body and pump body
standard	0.02 – 0.07 mm
limit for use	> 0.2 mm

Plunger Springs Inspection
1) Visually check the plunger Springs for wear, weakening or damage.
2) Replace with new ones if found to be defective.
3) With a spring tester, check tension of the plunger springs.

Plunger Springs Specifications
Spring length when free	51.5 mm
Limit for use	49.5 mm
Length compressed to 44 mm	Replace if spring tension < 13.3 kg
Allowed deviation from vertical	Replace if > 1.5 mm

Control Sleeve Clearance
1) Check the clearance between the flange of the plungers and groove in the control sleeves.

Control Sleeve Clearance
Standard	0.02 – 0.08 mm
Limit for use	> 0.12 mm

Plunger Barrels
1) Check the face of the plunger barrels in contact with the pump housing for distortion or damage. If necessary, correct with a hand milling machine.

Control Opinions Inspection
1) Check the gear for wear or damage and replace if found to be defective.
2) Discard the clamp screw and install a new one.

Control Rack Teeth Inspection
1) Check the control rack teeth for wear.
2) Check the control rack for bending by rolling it over a surface plate.
3) Replace the control rack with a new one if bending is noticeable.

NOTE:
1) Check the threaded portion of disassembled parts for damage and replace the parts as necessary.
2) Wash clean disassembled parts in kerosene.
3) Cleaner fuel ports in the pump body using compressed air.

Injection Pump Re-Assembly

When inspection is completed:
1) Separate the parts to be replaced from reusable parts.
2) Use new gaskets.
3) Prepare replacement gaskets for reassembly.

Delivery valve gaskets

Plunger Barrels
3) Aligned the groove in the plunger barrel with the floating dowel on the cover plate of the pump housing.
4) Install the plunger barrels into the pump housing.
5) Turn the plunger barrels to see if the Dowell is fitted into the corresponding groove properly.

Delivery Valve Assemblies
1) Assemble a new delivery valve gasket to the delivery valve assembly, using an extractor and a hammer.
2) Use own threaded end of the extractor against the gasket, when driving it into position.
3) Install on the plunger.
4) Check to be certain the upper face of the plunger barrels and the lower face of the valve seats are clean and free from foreign matter.
5) The delivery valve gaskets should be so installed that their face with heavily temporary is turned down.
6) Position the delivery valve spring on the delivery valves.
7) Tighten the delivery valve holder is, with a torque wrench, to specification.

Valve Holder Torque	3→0→3→0→3~3.5 kg-m

8) Tighten the lock plate bolts.

Lock Plate Bolts Torque	0.8 kg-m

Control Rack Installation
1) Insert the control rack into the injection pump housing from the governor side, so that the chamfered side is turned to the governor, and the teeth to the cover plate side respectively.
2) Fix the control rack in central position, so that the punch mark on the circumference of the control rack is centred between both ends of the pump housing.
3) If the control rack is not provided with the punch mark, set the control rack so that its ends are extended from the side face of the injection pump housing by 17.5 mm.
4) Hold the control rack in central position and engage the control pinions with the control rack teeth so that their slot is turned toward the reader.
5) Installed the control rack guide screws on the rear face of the injection pump housing.
6) Measure the full stroke of the control rack from the governor side to the automatic timer side, using a depth gauge of Vernier calipers.
7) If the measured value deviate from the specified stroke, read check setting of the control rack, and if necessary, adjust by this engaging and re-engaging control pinions.

Control Rack Full Stroke
Standard	21 mm

8) Install the upper spring seat in position with the flat face up.
9) Insert the plunger springs into the pump housing through the screw plug hole in the bottom face of the pump housing.
10) Assemble below at spring seat to the plunger, and insert these parts into the plunger barrel using a plunger insert.
11) The plunger should be so installed that the groove or the part number mark is pointed to the cover plate side (reed in the plunger lines up with intake and outlet port in the plunger barrel).

Tappet Assemblies Installation
1) Clamp the lower part of the tappet body with the tappet clamp.
2) Install it into the pump housing through the camshaft whole.
3) Fit the flange of the plunger into the slot in the control sleeve.
4) Assemble the tappet holder to the tappet by depressing the handle on the tappet insert.
5) Support the tappet in that position.

Camshaft Installation
1) Insert the camshaft into the pump body from the automatic timer side, so that its end with the assembly mark is turned to the governor side.
2) Check that the feed pump fitting hole is in alignment with the feed pump drive cam.
3) Mount the governor housing and gasket to the injection pump housing.
4) Install the bearing cover and gasket on the injection pump housing.
5) Turn the camshaft and remove the tappet insert.
6) Check operation of the tappets.
7) Apply adhesive to the threaded portion of the screw plug.
8) Install and securely tightened the screw plug.
9) Check the effort required to slide the control rack using a port scale.
10) Take measurements by pulling the control rack with the plunger in each barrel held at the Top Dead Centre.

Control Rack Friction
standard	< 150g

11) Install the flyweight assembly on the injection pump camshaft.

Flyweight Round Nut Torque	5 - 6 kg-m

12) Install the governor cover.

13) When reassembly of the injection pump parts is completed, make the necessary adjustments with the injection pump mounted to a pump tester.
14) To make a test, install pump tester coupling in place of the injection pump gear.
15) Alignment the key groove in the automatic timer with the key on the camshaft and installed the automatic timer.
16) Install the spring washer and tightened the round nut securely.
17) With the special range hold the flyweight holder for turning and tightened the round that securely using a wrench.

Flyweight Round Nut Torque	6 - 7 kg-m

18) Connect the injection pump to a pump tester and make adjustments by following the steps outlined (see below).
19) When adjustment operation is completed, remove the pump tester coupling.
20) Install the pump bracket with the setting marks aligned.
21) Install the pump side coupling and year on the camshaft.
Injection Pump Re-assembly

Reassemble the injection pump parts in the reverse order of disassembly.

Installation of Plunger Barrels
1) Install the plunger barrel so that the groove in the plunger barrel is aligned with the indexing pin on the injection pump housing.

Installation of Delivery Valves
1) Install a new valve gasket on the delivery valve and mount the delivery valve on the injection pump.
2) Delivery valve gasket should be so installed that its face with heavy chamfering on the inner edge is turned down.
3) Install the delivery valve spring and tighten the delivery valve holder to spec.

Delivery Valve Holder Tightening Torque	3 – 3.5 kg-m

Installation of the Pinions
1) Install and fix the control rack in position, so that its end is projected from the drive side face of the injection pump by 3.5 mm.

2) Install the pinions with the slot side up.
3) Move the control rack and check that its travel in both direction is equal.
4) Hold the plunger with pincers and inset it into the plunger barrel together with the lower spring seat.
5) Plungers should be installed so that the mark on the flange is turned down.

Camshaft Installation
1) Install the distance ring, shim and bearing on each end of the camshaft in the order mentioned.
2) Install these parts into the injection pump.
3) Apply generous amounts of adhesive 29941-072 to the joining face of the bearing cover and injection pump and install the bearing cover.
4) Measure the camshaft end play.
5) Adjust, using shims, to 0.03 – 0.05 mm using shims as needed.

Tension Lever Installation
1) Install the control level assembly in position with the lever shaft.
2) Hook the governor spring to the swivel lever.
3) Connect the swivel lever to the lever shaft, using shim, spring washer and nut.
4) Install the full-load stopper.
5) Connect the control rack to the forked position of the link with the pin.
6) Connect the governor spring to the tension cover and fasten the parts together with the shaft.

Flyweight Installation
1) Install the shim and sleeve on the camshaft.
2) Install and fix the flyweights with the nuts.

Flyweight Nut Torque	5 - 6 kg-m

3) Check that travel of control rack is 11 mm. If the travel is more or less, adjust by means of shim(s) between the sleeve and the guide lever.

Adjustment of the Injection Pump

Adjustment of the injection pump requires use of the essential pump tester and attachment:	Engine model 2AB1B
pump assembly number – 4302-851 (Isuzu pn 5-15600-212-0)
pump model	- 4300-223 (Isuzu pn PES2K65A120/3LA2NP23)

Injection Pump Data
Direction of Rotation	counterclockwise, as viewed from drive side
Nozzles	500-108 (np-DN0SD211)
Nozzle Holders	5780-201
Nozzle valve opening pressure	120 kg/cm2
Injection Pipes	ID 2ø x OD 6ø – length 600 mm
Pressure of Delivery	1.6 kg/cm2
Testing Fuel	JIS Grade 2 kerosene
Apply 180 cc pump oil to the injection pump

Adjustment of Injection Timing
Prestroke	#1 barrel 2.1± 0.05 mm lift
barrels are numbered #1, #2 from drive side
Injecting order	1270'±30' – 290'±30' – 1
Tappet clearance	> 0.03 mm

Adjustment of Injection Volume

Control rack position	Pump Speed / rpm	Mean volume of injection (mm3/st)	Variance / (%)	Remarks
9.5 mm	750	43 ± 1.3	± 4	standard
9.5 mm	1200	43.5 ± 1.0	± 2.5	standard
About 5.5 mm	350	8.0 ± 1.0	± 14 or 1.4	standard

3AB1 Adjustment of Timing

Control Rack / Position / (mm)	Pump / Speed / rpm	Volume / of Injection / (cc/1000st.)	Variance / %	Remarks
12.0	750	42 ± 0.8	± 2	Standard
8.0	750	12 ± 0.6	± 4
12.0	900	43 ± 1.6	± 3
± 8.0	475	8 ± 1.0	± 14

1) Mount the injection pump to a pump tester via the pump fixture.

Pump Tester	Pump fixture PN#
5702 - 021
5702 - 011
5760 – 001 (50 ∞ )	5781 - 005
5760 – 002 (60 ∞ )	5781 - 005
5700 - 011
E F E P 5 C
E F 8345 C	5730 - 501

2) Remove the cap on the end of the injection pump and install the control rack measuring device (PN# 5782-601) in place.
3) Push in on the pinion in direction of the fuel stop and calibrate the main scale and vernier scale to zero.

Adjustment of injection Timing
1) Connect the high pressure pipes from the pump tester to the injection pump and turn the camshaft to bring the tappet in the No1 barrel to Bottom Dead Centre.
2) Hold the testing probe of the plunger stroke measuring device (PN# 5782-402) in contact with the upper face of the tappet and push the measuring device against the cover plate.
3) Calibrate the dial indicator to zero and turn the camshaft slightly in both directions and check that the indicator needle stays still.
4) Check to be certain that the tappet in No1 barrel is (still) at Bottom Dead Centre.

5) Turn the camshaft slowly counterclockwise, as viewed from the drive side and make any necessary adjustment so that the fuel stops flowing out from the nozzle holder overflow valve when the dial indicator needle reaches the 1.75 ± 0.05 mm point.

6) To adjust injection timing, proceed as follows:
7) Hold the cam at its uppermost position and insert the spring holder (PN# 57931-410) into the groove in the tappet body.
8) Turn the cam to bottom position and adjust thickness of the shim fitted to the upper face of the tappet.
9) Turn the camshaft slowly counterclockwise (as view from the drive side) and adjust the injection timing of the remaining barrels in the sequence 1-3-2, so that the fuel stop point of each barrel is set at an angle of 1200 ± 30 apart.

Adjustment of Injection Volume
1) To adjust the fuel injection volume, make a test using injection nozzles that are adjusted to a pressure of 120 kg/cm2.
2) Move the control rack from the full-load position to the specified points. (Refer to 4-1-27 on page 4-1-28)
3) Operate the injection pump at the specified speed and adjust the injection volume of each barrel to specifications.
4) To adjust injection volume, proceed as follows:
5) Loosen the control pinion clamp screw and turn the control sleeve counterclockwise to increase the volume and clockwise to reduce the volume.

Adjustment of

1981 Manual	Isuzu Pisces
1	Dust cover	=	18	Dust cover (1) 42039
2	Joint bolt	=	19	Hollow bolt (1) 42037
3	Gasket	=	11	Crush washer (4) 42038
4	Joint nipple	20	Adaptor (1) 42031
5	Spring	=	16	Spring (2) 42030
6	Check valve	15	Check valve (2) 42029
7	Washer	=	14	O-ring (2) 42033
8	Housing	=	1	Feed pump assembly (1) 43020
9	Pin	=	8	Pin (1) 42027
10	Roller	=	9	Roller tappet (1) 42026
11	Tappet guide	7	Guide (2) 42028
12	Tappet	=	6	Tappet body (1) 42025
13	Snap ring	=	10	Snap ring (1) 42040
14	Washer	=	11	Crush washer (4) 42038
15	Joint bolt	=	12	Filter (1) 42036
13	Hollow bolt (1) 42035
16	Push-rod	=	(not numbered)
17	Piston	=	2	Piston (1) 42021
18	Spring	=	3	Spring (1) 42022
19	Washer	=	4	Gasket (1) 42024
20	Plug screw	=	5	Cap plug (1) 42023
21	Priming pump Assembly 17 Priming pump (1) 42034
(not shown)	21	O-ring (1) 42033

Fuel Feed Pump

Description
The feed pump is driven by an eccentric cam on the injection pump camshaft and delivers fuel to the injection pump.

It is equipped with a priming pump to permit the manual feeding of fuel to the injection pump.

The feed pump has the intake port on the lower side, and the outlet port on the upper side.

When the engine load is removed and delivery of fuel becomes excessive, pressure of fuel builds up behind the piston and holds the piston in suspension – thereby regulating further delivery into the injection pump.

Inspection Prior to Disassembly
1) With the fuel pump removed from the injection pump, check the fuel pump in the following manner:
2) Overhaul the feed pump if found to be defective.

Piston
1) Depress the tappet with finger to see if it can be pushed in.
2) If it cannot be pushed in, either the piston or the push-rod is sticking or is seized up.

Priming Pump
1) When the cap is screwed out, the priming pump should snap out (pushed by the action of the spring).
2) If not, parts of the pump are sticking or are seized up.
3) Perform feed pump test - see below.

Feed Pump Disassembly

1) Remove the joint bolt (2 or 15).
2) Screw out the gauze filter from the intake side joint bolt.

Check Valve Removal
1) Remove the priming pump (21) and outlet side joint nipple.
2) Remove the check valve spring (5) and check valves (6).
3) NOTE: Carefully note their fitting positions to insure reassembly in their original positions.

Tappet Removal
1) Remove the snap ring (13) with a scriber or equivalent.
2) NOTE: When removing snap ring, raise free end, as the other end is fitted into the hole of the body.
3) Remove the tappet assembly (12, 11).
4) If it does not come out easily, drive out with a rod and a hammer, being careful the guide does not fall.

Piston Removal
1) Remove the piston chamber plug (20).
2) Take out the piston spring (18), piston (17) and push-rod (16).

Tappet Assembly Disassembly
1) Remove the tappet guide (11) and pull out the roller pin (9, 10).