(LLR) plans for the simulation of the SiW ECAL in a reduced version ILD
1. 2 mains ways to reduce the cost of the SiW ECAL
  1. Redution of Radius with fixed R/Z ratio
    1. ⇒ TPC, ECAL (∝ R²), HCAL, Coil, Yoke, Cavern, (tunnel)
    2. R 1800→1400 @ Nlayers= “30”: JER +10 %
  2. Reduction of number of layers
    1. Nlayers “30” → “20” @ R=1800: JER + 9%
    2. Nlayers “30” → “20” @ R=1400: JER + 6%
2. ⇒ Simulation modifications for reduced radius & layers.

---
(LLR) plans for the simulation of the SiW ECAL in a reduced version ILD
1. Ideas only : all dimensions to be refined by mechanical model
2. Reduced radius ~144cm (to be validated by a modified model of endcaps)
  1. Largers Wafers: 8” (would be OK from HPK, LFoundry)
    1. Wafer side: ~10 → ~13 cm; Alveola ~20→~26 cm;
      1. Barrel: 5 modules of 3 (was 5) alveola ⇒ LBarrel ~390cm
      2. Endcaps: with R(ECAL Ring) = 40cm (?) → R = 40+4*26 ~ 144cm
3. Nlayers = 24 = 16 + 8 (single and double W thickness)
4. Wafer thickness 500→ ~700μm
  1. Improved σ(Eγ) ∝ 5√t ⇒ ~recovery of Nlayers effect
5. Option to render the 1st Si layer standard ⇒ SEcal06 driver ?
  1. 1 layer of W in front 1st alveola ⇒ no preshower; keep option to not have it.
  2. more regular structure: n1/2×(W1+[Si+W1+Si]) + n2/2×(W2+[Si+W2+Si])
    1. Now : [Si+W1+Si] + (n1-1)/2×(W1+[Si+W1+Si]) + W1 + n2/2×([Si+W2+Si] + W2)
  3. For hybrid: alteranate Si and Sc alveola [*]
6. (Implementation of SEcal05 in DDHEP based on S. Lu implementation of SEcal04 + tests)
on-going:
D. Jeans: correct & improve GEAR output.
E. Becheva & D. Yu : review documentation & code (endcaps, ...)