Experiment 7: AC Circuits

Objectives:
1. To measure the AC impedance of passive electronic components such as resistors, inductors and capacitors.
2. To understand the dependence of the AC impedance on the frequency.
3. To explore the resonance phenomenon in an LCR circuit.

Lab procedure:
For the first circuit, we'll measure the voltage across the resistor and calculate the current at various frequencies. Then we'll measure the voltage drop across the entire circuit which will allow us to calculate the total impedance of the circuit.
We'll use a similar procedure for the second circuit, which has an additional component (acapacitor). We'll plot Z versus f^2 for the first circuit, and I versus f for the second one.

Theory and formulas:

We'll use three types of passive components:
- resistors oppose the flow of currents through them. with a
  (1) V_R = I R
- capacitors store electric charge Q , voltage drop across them depends on capacitance C and charge:
  (2) V_C = Q over C
- inductors resist changes in the current in the circuit; inductance L is a constant.
  (3) V_L = L { %DELTA I } over { %DELTA t }
In an AC circuit, the root mean square voltage is V_rms = V over { sqrt{2} } , and the peak voltage V is related to peak current I :
(4) V = I X
where the AC impedance X can be calculated for:
- resistors:
  (5) X_R = R
- capacitors:
  (6) X_C = 1 over { 2 %pi f C }
- inductors:
  (7) X_L = 2 %pi f L
The total impedance of a series combination of a resistor, capacitor, and inductor is:
(8) Z = sqrt{ R^2 + (X_L - X_C)^2 }
also,
(9) Z = V over I
If in such a circuit, X_L = X_C , then the total impedance is minimized, because of (8), and so the total current through the circuit is maximized. This happens when the frequency is
(10) f = 1 over { 2 %pi } sqrt{ 1 over {LC} }
,which is the resonance frequency.