Contents
- Motivation
- Theory
  1. RLC theory – Resonance frequency / Impedance transformation / Series vs. parallel notation / The attenuator / Equivalent circuits
  2. Common mode and differential mode signals
  3. Single-ended and differential signals
  4. Electromagnetic theory basics – Inductance confusion / HF effects / Radiation
  5. Control theory basics – Transfer function / Graphical methods / Rules of thumb
Design issues
  1. What frequencies do I have?

---
Motivation
Different meanings of “good” PCB:
  1. the circuit works as expected,
  2. the circuit is not disturbed by external events/noise (fluorescent lamp, relay switching, CRT monitor, mobile phone, etc.),
  3. the circuit is not disturbing its surrounding (radio receivers, etc.),
  4. the circuit passes applicable ESD and EMC standards (both conducted and radiated),
  5. the circuit provides clean measuring possibilities.
- Different boards are designed under completely different aspects (e.g. ATE handler adapter vs. chip-level EMC compliance test PCB).
- Reciprocity principle: a circuit that is emitting at a given frequency, is likely to be susceptible for external disturbances at this frequency, i.e. broadband noise generators often prove to be sensitive.

---
RLC theory I – Resonance frequency I
%omega_0% = {1} over {sqrt{L cdot C}}
- RLC tank (both series and parallel) have resonant frequency at
- Quality factor is generally defined by
- formulas differ for series and parallel RLC tanks:
- Resonant frequency is defined as the frequency f0, where the imaginary part of the total admittance (or impedance) is zero, that is Im{Y(f0)}=0, or alternatively Im{Z(f0)}=0. This is the frequency, an oscillator in steady state is resonating.
- A resonant tank without energy restoring produces an exponentially decaying oscillation with the tank's natural frequency, for that fn<f0.
Q=%omega% cdot {{alignc "stored energy"} over {"average power dissipated"}}
Q_"0,series" = {1} over {R} cdot {sqrt{L over C}} = {%omega%_0 cdot L} over {R} ~~~~~~~~ Q_"0,parallel" = R cdot {sqrt{C over L}} = %omega%_0 cdot R cdot C
%omega%_"n" = sqrt{{1} over {L cdot C} cdot left( 1 - {1} over {4 Q_0^2} right) } ~~~~ %omega%_"n,series" = sqrt{{1} over {L cdot C} - {R^2} over {4 L^2}} ~~~~ %omega%_"n,parallel" = sqrt{{1} over {L cdot C} - {1} over {4 R^2 cdot C^2}}

---
RLC theory I – Resonance frequency II
- The damping constant of a naturally damped oscillation is given as:
- Definition of the logarithmic decrement Λ:
- Quality factors:
- For both series and parallel tank the following holds:
- The 3dB bandwidth is defined as follows:
%beta%_"series" = {R} over {2 L} ~~~~~~ %beta%_"parallel" = {1} over {2 R cdot C}
%LAMBDA% = ln left( {V_"peak #i"} over {V_"peak with same sign #i+1"} right)
Q_"n,series" = {%omega%_"n" cdot L} over {R} ~~~~~~~ Q_"n,parallel" = %omega%_"n" cdot R cdot C
Q_"n"={%omega%_"n"} over {2 %beta%}={%pi%} over {%LAMBDA%}=sqrt{Q_0^2 - {1} over {4} } %LAMBDA% = {%pi%} over {Q_"n"}= %beta% cdot {{2 %pi%} over {%omega%_"n"}} " " %omega%_"n"^2 = %omega%_0^2 - %beta%^2
alignl lline Z(f_1) rline = lline Z(f_2) rline = Z(f_0)/sqrt{2} " for parallel tank" newline alignl lline Z(f_1) rline = lline Z(f_2) rline = Z(f_0) cdot sqrt{2} " for series tank"
alignl B=left lline f_2 - f_1 right rline = {f_0} over {Q_0} " with" f_1 "and" f_2 "defined as "
"for both tanks " f_0^2=f_1 cdot f_2

---
RLC theory I – Resonance frequency III
- Impedance and bandwidth of a series tank with C=100nF, L=1µH, R=2Ω.
- Resonance at f0=503.3kHz
- Minimum Z0 impedance
  occurs at resonance
  Z0=R=2Ω=6dBΩ
- 3dB impedance magnitude
  and 45° phase change at
  f1=368.7kHz
  f2=687.0kHz
  B=318.3kHz
- Below f0 capacitive
  behavior, above f0
  inductive behavior.
Z_0 cdot sqrt{2}
f1
f2
f0
3dB
Z0
Phase
capacitive inductive
B
0.1

---
RLC theory I – Resonance frequency IV
- Naturally decaying series tank with C=100nF, L=1µH, R=2Ω and the capacitor initially
  charged to VC0: f0=503.3kHz, fn=477.5kHz, Q0=1.58, Qn=1.50, Λ=2.09, β=106 1/s
- Notice the 5.1% frequency and Q deviation from the undamped oscillation case.
- The current and the capacitor voltage are given with tan(ϕ)=ωn/β, ϕ=71.6°:
- Naturally decaying parallel tank with C=100nF, L=1µF, R=5Ω and the capacitor initially
  charged to VC0: f0=503.3kHz, fn=477.5kHz, Q0=1.58, Qn=1.50, Λ=2.09, β=106 1/s
- Notice the identical values to the series tank case (see RLC theory III – Series vs. parallel notation II for details).
- The capacitor current and voltage are (with ϕ=71.6°, as for the series tank):
- Notice the identical formulas for series and parallel tanks except for the additional –2ϕ in the sinus argument and the flipped sign.
i(t)=-V_"C0" cdot C cdot { {%omega%_0^2} over {%omega%_"n"} cdot e^{-%beta cdot t} cdot sin(%omega_"n" cdot t) }
v_"C"(t)=V_"C0" cdot {{%omega%_0} over {%omega_"n"}} cdot e^{-%beta cdot t} cdot sin(%omega_"n" cdot t + %phi%)
i_"C"(t)=V_"C0" cdot C cdot { {%omega%_0^2} over {%omega%_"n"} cdot e^{-%beta cdot t} cdot sin(%omega_"n" cdot t -2 %phi%) }
v(t)=-V_"C0" cdot {{%omega%_0} over {%omega_"n"}} cdot e^{-%beta cdot t} cdot sin(%omega_"n" cdot t - %phi%)

---
RLC theory I – Resonance frequency V
Series resonance plots (tank parameters from previous slide: C=100nF, L=1µH, R=2Ω). Shown is the naturally decaying capacitor voltage (red), the undamped oscillation capacitor voltage (blue) and the decaying tank current (green).
Time / µs
Voltage / V
Current / A
Vpeak#1
Vpeak#2
Current
T0
Tn

---
RLC theory I – Resonance frequency VI
Series vs. parallel resonance plots (tank parameters from previous slides: C=100nF, L=1µH, series R=2Ω, and parallel R=5Ω). Voltage plots.
Time / µs
Voltage / V
series
parallel

---
RLC theory I – Resonance frequency VII
Series vs. parallel resonance plots (tank parameters from previous slides: C=100nF, L=1µH, series R=2Ω, and parallel R=5Ω). Current plots.
Time / µs
Current / A
series
parallel

---
RLC theory I – Resonance frequency VIII
- For a parallel LC tank with non-ideal inductor and capacitor the resonant frequency is:
- Simplifications
  1. For ideal LC (RL=0, RC=0)
     or RL=RC:
  2. For ideal L (RL=0):
  3. For ideal C (RC=0):
Numerical calculation: L=10µH, RL=1Ω, C=100nF, RC=0.2Ω yields:
fideal=159.15kHz and freal=158.39kHz (0.48% frequency shift is far below component tolerances). Significant for RC snubber networks (RC=3Ω yields 166kHz or +4.8%).
%omega%_0^2 = {L - R_"L"^2 cdot C} over {L cdot C cdot left(L - R_"C"^2 cdot C right) }
%omega%_0^2 = {1} over {L cdot C}
%omega%_0^2 = {1} over {L cdot C - R_"C"^2 cdot C^2}
%omega%_0^2 = {1} over {L cdot C} - {R_"L"^2} over {L^2}

---
RLC theory II – Impedance transformation I
Ideal LC high-/lowpass configurations perform (frequency dependent) impedance transformation. For properly designed filters:
  1. series-parallel CL or LC elements transform the input impedance upward,
  2. parallel-series CL or LC elements transform the input impedance downward.
  3. Constant impedance (e.g. 50Ω) needs a T or Π (Pi) topology filter (low-, high- and bandpass and notch filter configurations possible by cascading series-parallel and parallel-series elements).
  4. Simple dimensioning is possible with the Smith chart (out of scope for this document).

---
RLC theory II – Impedance transformation II
- Series-parallel transformation: if element A is a capacitor, then element B has to be an inductor and vice versa. Z0 is real (e.g. 50Ω).
- Using normalized variables: a=abs(Im{ZA})/Z0, b=abs(Im{ZB})/Z0
- With b=(1+a2)/a we get Z1=Z0∙(1+a2)
- Example: CL highpass for transforming Z0=50Ω to Z1=75Ω at f=10MHz
- a=sqrt(Z1/Z0-1)=0.707, b=(1+a2)/a=2.121
- ZA=-j∙a∙Z0 → C=1/(2∙π∙f∙a∙Z0)≈450pF
- ZB=j∙b∙Z0 → L=b∙Z0/(2∙π∙f)≈1.7µH
- Backdraws: the higher the conversion ratio, the more narrowband. LC elements usually not E12.
- Could have been done with a 25Ω series resistor in a broadband manner, but noisily.
Z0
ZA
ZB
Z1>Z0

---
RLC theory II – Impedance transformation III
- Parallel-series conversion: if element A is a capacitor, then element B has to be an inductor and vice versa. Z0 is real (e.g. 50Ω).
- Using normalized variables: a=abs(Im{ZA})/Z0, b=abs(Im{ZB})/Z0
- With b=a/(1+a2) we get Z1=Z0∙a2/(1+a2)
- Whether element A is chosen as a capacitor or as an inductor is determined by practical issues (valid for for both impedance upconversion and downconversion):
  1. Is a DC feed needed from Z0 to Z1 or alternatively, can one port DC shorted by an inductor?
  2. If no care for DC is necessary: for parasitic signal filtering, do I need a highpass or a lowpass?
Z0
ZB
ZA
Z1<Z0

---
RLC theory II – Impedance transformation IV
- For broadband noiseless impedance transformation a (self-wound) transformer may be utilized due to the well-known equations for the ideal transformer with n as the winding count:
- Solving and rearranging yields:
- Transformation works as long as	therefore the transformer has to be designed accordingly (that is, for example a large number of windings). At high frequencies the winding capacitance deteriorates the impedance transformation.
V_1 cdot I_1 = V_2 cdot I_2 newline I_1 cdot n_1 = I_2 cdot n_2
"by defining"~ Z_1 = {V_1} over {I_1}~ "and"~ Z_2 = {V_2} over {I_2}
{Z_2} over{Z_1} = left({n_2} over {n_1} right)^2
%omega% cdot L_"winding" >> R_"load"
I1
I2
V2
V1

---
RLC theory III – Series vs. parallel notation I
- A complex impedance can be realized with both series and parallel connected elements. So a transformation between series and parallel notation exists.
- The transformation yields frequency-dependent values.
- Simplifications:
  1. For XS >> RS:
  2. For RP >> XP:
  3. For RS >> XS:
  4. For XP >> RP:
R_"P" approx {X_"S"^2} over {R_"S"} ~~~~ X_"P" approx {X_"S"}
R_"S" approx {X_"P"^2} over {R_"P"} ~~~~ X_"S" approx {X_"P"}
R_"P"={R_"S"^2+X_"S"^2} over {R_"S"} ~~~~ X_"P"={R_"S"^2+X_"S"^2} over {X_"S"}
R_"P" approx {R_"S"} ~~~~ X_"P" approx {R_"S"^2} over {X_"S"}
R_"S"={R_"P" cdot X_"P"^2} over {R_"P"^2 + X_"P"^2} ~~~~ X_"S"={R_"P"^2 cdot X_"P"} over {R_"P"^2 + X_"P"^2}
R_"S" approx {R_"P"} ~~~~ X_"S" approx {R_"P"^2} over {X_"P"}
RS
j∙XS
RP
j∙XP

---
RLC theory III – Series vs. parallel notation II
- The same principle applies to resonant tanks.
- Two tanks behave the same if they have the same resonance frequency and the same quality factor.
- For the reactive component values it means for the simplest case, the component values stay the same during transformation (Lseries=Lparallel and Cseries=Cparallel) due to:
- The resistors are transformed as follows:
- Simplification for the simple case of identical reactive component values:
%omega%_"0,series" = %omega%_"0,parallel" " and " Q_"0,series" = Q_"0,parallel"
L_"series" cdot C_"series" = L_"parallel" cdot C_"parallel"
R_"series" = {1} over {R_"parallel"} cdot sqrt{{L_"series" cdot L_"parallel"} over {C_"series" cdot C_"parallel"}}
R_"series" = {1} over {R_"parallel"} cdot {{L} over {C}}

---
RLC theory IV – The attenuator
- The attenuator structure has a frequency-independent transfer curve. This is used in oscilloscope voltage probe tips for wideband 1:10 attenuation (with a=9).
- Transfer characteristics:
- Purely real transfer function, no phase delay introduced. Signal fidelity is preserved (the price is an attenuated signal and reduced signal to noise ratio).
{V_"out"} over {V_"in"} = {1} over {1+a} " with " a>0
C
a·R
a·C
R
Vin
Vout

---
RLC theory V – Equivalent circuits I
Physical R, L, C components are not purely resistive, inductive or capacitive, but a mixture of all these elements:
capacitor
RESR
LESL
C
Rd
resistor
LESL
Ceq
R
inductor
L
Ceq
RESR
transformer
L1
CW1
RW1
LS1
LS2
L2
CW2
RW2
L12
CC
RC

---
RLC theory V – Equivalent circuits II
- ESR=equivalent series resistance; ESL=equivalent series inductance.
- For simple estimations some elements of the equivalent circuit are ignored.
  1. For capacitors: The dielectric leakage resistor Rd is either omitted or transformed into the ESR (see RLC theory III – Series vs. parallel notation).
  2. For resistors: the capacitor Ceq is omitted.
  3. For inductors: the capacitor is omitted far below the self resonance frequency.
  4. For transformers: Winding capacitors CWx and coupling capacitor CC are generally ignored. The core losses resistor RC and the winding resistors RWx are often omitted. The secondary stray inductance LS2 is absorbed into L2. For ideal transformers both LS1 and LS2 are omitted.
Note, that the equivalent elements depend on anything you can think of (frequency, temperature, component's age, voltage, humidity...). Note furthermore, that these dependencies are only of academic interest in the overwhelming majority of cases as they are below component tolerances. If this is not the case and you checked “Practical issues XII – Tolerances and aging”, you should think about your design once again.

---
RLC theory V – Equivalent circuits III
- Nonideal transformer magnetics are either characterized with leakage and magnetizing inductance (mainly US literature) on one hand and with coupling factor on the other hand (simulators and German literature).
- Physically speaking, not the whole magnetic flux generated by primary current I1 is crossing the secondary winding. Thus, this portion of the flux does not contribute to energy transfer and is considered as leakage. This leakage flux is generated by a non-coupled inductor LS1.
- The flux reaching the secondary winding is generated by the magnetizing inductance Lm.
- The two primary inductances are connected in series, as there is only one current that is flowing in each turn equally. So the total/measurable primary inductance is L11=LS1+Lm.
- The magnetizing flux reaches the secondary coil and induces a voltage according to Faraday's law by the mutual inductance L12.
- The other methodology introduces the coupling factor k instead of the stray inductance. The imperfect coupling is modeled by reducing the mutual inductance by factor |k|<1.

---
RLC theory V – Equivalent circuits IV
- Introducing the primary and secondary winding turn number n1 and n2 and dealing only with inductances:
- The voltage ratio formula approximation completely ignores R and C components, and is still valid for s·LSi <<ZLoad only (with i=1,2).
- Schematic with magnetizing inductance (left) and nonideal magnetic coupling (right).
L_1 equiv L_"m"=L_12 cdot {{n_1}over{n_2}}~~~~~ L_"ii"=L_"Si"+L_"i" " with " i=1,2 ~~~~ L_"i"=L_"ii" cdot k^2 ~~~~~ L_"Si"=L_"ii" cdot left(1-k^2 right) newline alignl k={" "L_12} over {sqrt{L_11 cdot L_22}} ~~~~~ {n_2} over {n_1} = sqrt{{L_22} over {L_11}} =sqrt{{L_2} over {L_1}}~~~~~~ {V_2} over {V_1}=left({n_2} over {n_1}right)_"eff" approx k cdot {{n_2}over{n_1}} = k cdot sqrt{{L_22} over {L_11}} ={L_12} over {L_11}
L1=Lm
LS1
L2
LS2
ideal
transformer
L11
L22
0<k<1
k=1
I1
I2
I2
I1
V2
V1
V1
V2
n1 : n2
n1 : n2

---
Common mode and differential mode signals I
- Theory distinguishes common mode (CM) and differential mode (DM) signals.
- Easier to analyze and to take countermeasures → CM and DM filters.
- Ideal case I+ +I‒=0. Unfortunately, this doesn't
  happen in real life.
- Real case I+ + I‒ = Ileak
- By definition
  ICM = I+ + I‒ and
  IDM = I+ ‒ I‒
- Solving the equation system yields
  I+ = ICM/2 + IDM/2 and
  I‒ = ICM/2 ‒ IDM/2
V
Module
I+
I‒
+
‒
V
Module
I+
I‒
+
‒
ILeak
ILeak
Z1
Z2
power earth

---
Common mode and differential mode signals II
- CM and DM currents can be measured at the harness conveniently by current probes (e.g. Hall sensor probes). No need to locate Z1 or Z2.
- CM probe measures ICM and DM probe measures IDM.
- Concept is utilized e.g. at bulk current injection (BCI) tests with CM and DM current injections.
V
Module
IDM/2
+
‒
Z1
Z2
power earth
ICM/2
ICM/2
IDM/2
ICM
ICM
CM probe
DM probe

---
Common mode and differential mode signals III
- By measuring CM and DM current, proper filter type can be selected.
- Warning: filter (and other) asymmetries convert CM signals to DM signals.
- Filters F1 and F2 work both for CM and DM.
- CM and DM filter types:
  1. inductive common mode filter CM1,
  2. inductive differential mode filter DM1,
  3. capacitive differential mode filter DM2,
  4. differential mode RC snubber network (lossy differential mode capacitor).
V
+
‒
C
L
L
F1
F2
C

---
Common mode and differential mode signals IV
- CM and DM filters may be cascaded in a practical manner (take care for electrical and magnetic coupling – e.g. use toroid cores). Example from IEEE Trans. Power Electron., vol. 29, no. 5, p. 2339, May 2014 for a 10kW 3-phase 2-level VSI switching at 20kHz.
- Select the filter type according to (measured) CM and DM noise to be suppressed. The filters are listed with their equivalent (not coupled) component values for common and differential modes.
V
+
‒
4.7µF
56µH
2.35mH
L
L
CM1
DM1
DM2
47nF
C
F2
9.4µF
3Ω
snubber

---
Single-ended and differential signals I
- Single-ended: source with one output terminal connected to the load (and some return current path).
- Differential: source with two output terminals driving two signals 180° out of phase with equal amplitude A. At any place x between the source and the load Φ+(x)=Φ−(x)+180° and A+(x)=A−(x) . That is, in the ideal case, there is no return current in a third signal/ground line. This is achieved by using symmetrical elements and layout.
- Differential signaling reduces sensitivity for common mode disturbances, and vice versa, differential signaling generates no common mode signal, even in the presence of a power earth. The price is the extended complexity of the circuit and the problem of generating signals with exactly 180° phase shift and exactly the same amplitude.
V+
Load
IS+
IS‒
ILeak2=0
Z1
Z2
ILeak1=0
V−
Z3
Z3
ILeak3
IL+
IL‒

---
Single-ended and differential signals II
- What is better: a differential signal or a (possibly shielded) single-ended signal?
- For coupling we're interested in the reactive near field, as the distance from the cable/track is less than λ/(2π), roughly 48cm (19”) free space for 100MHz.
    1. A differential signal in twisted pair (shielded or unshielded) cable (STP/UTP) has ideally zero near field, if the twisting is <λ/10. For untwisted parallel PCB tracks the fields don't cancel perfectly, so they have both capacitive and magnetic coupling to neighbor tracks.
    2. Even a non-sinusoidal single-ended signal in a coax or twisted pair cable has ideally zero near field, as long as no leakage currents exist. Otherwise time- and position-dependent near field exists.
  2. The input supply voltage ripple generated by a differential driver is ideally zero.
  3. If analog unipolar differential signals are required, depending on the load, an adequate common mode voltage (e.g. VDD/2) with large current source/sink capability may be needed.
  4. A single-ended coax cable is far the easiest to handle, if the application does not require differential signaling (use STP in the latter case for best EMC performance).

---
Single-ended and differential signals III
An analog wideband single-ended to differential converter (balun=balanced-to-unbalanced) can be realized by a center-tapped transformer with n:n windings. Of course, signal transformation by different primary and secondary winding count is also possible.
  1. The center-tapped transformer usually provides better matching than two separated secondary windings. But even this structure may need manual symmetry tuning.
  2. Check commercially available baluns/transformers (“stromkompensierte Spulen”) for their imbalance properties.
  3. If common mode voltage is not an issue, the center tap can be simply grounded. Otherwise, the common mode voltage can be set in a convenient way by a voltage source with low output impedance.
  4. Alternatively, two OpAmps can be used: one in inverting, the other in non-inverting configuration. For better matching, do not omit the non-inverting OpAmp.
Differential to single-ended conversion can be done by a simple transformer.
  1. Alternatively, an OpAmp can be used with four matched resistors. If the input impedance has to be high, an instrumental amplifier (InA) shall be used.

---
Single-ended and differential signals IV
Analog single-ended to differential conversion and vice versa.
  1. Usually, trimming is required for the resistors.
  2. For single-ended to differential: use a dual-OpAmp device for matching reasons.
V
+
–
VCM
V+
V−
+
–
+
–
+
–
R
R
V+
V−
(bipolar)
R
R
R
R

---
Single-ended and differential signals V
- For unipolar digital signals a fast inverter and a comparator can be used. Do not omit the input (leftmost) inverters, they reshape the signal edges and decouple the differential signal noise from the input. Use a hexa inverter device for matching reasons.
- If the delay mismatch is critical, use a hexa inverter device for matching reasons and the lower circuitry. This minimizes the phase error, but has a high current consumption at the signal edges. Select the resistor value to about five times the inverter output resistance. Resistor selection/tuning shall be done by watching the signals on an oscilloscope.
- The center-tapped transformer and a dual-inverter for the differential output signal can also be used.
V+
V−
V+
V−
+
–

---
EM theory basics I – Inductance confusion I
- Different kinds of inductance: self, mutual, loop inductance (to complicate things, all of them are frequency dependent) in addition to internal and
  external inductance.
- Self inductance is the inductance of a conductor #1 defined by
  with A1 as the magnetic potential caused by current I1 flowing
  in the conductor; J1 the current density and dV1 the differential
  volume element of the conductor.
- Mutual inductance describes the inductive coupling between two
  conductors. By definition the current direction is the same in both
  conductors for positive mutual inductance. Note, that for our
  practical cases L21=L12. Mutual inductance for perpendicular
  conductors is ideally zero.
- Loop inductance is the complete inductance of two conductors, measurable at one end under the condition I1+I2=0 (e.g. the two conductors are shorted at the other end).
  Due to opposite current direction in the conductors: L21=L12<0.
L_11={int A_1 cdot J_1 cdot "d"V_1} over {I_1^2}
L_21={int A_1 cdot J_2 cdot "d"V_2} over {I_1 cdot I_2}
L_"loop"=L_11-L_12-L_21+L_22

---
EM theory basics I – Inductance confusion II
Self inductance can be separated into internal and external inductance.
  1. Internal inductance is attributed to the magnetic field within the conductor,
  2. external inductance is attributed to the magnetic field external to the conductor.
- The magnetic field outside the conductor does not change with skin effect, but the field within the conductor is reduced (the center of the conductor is magnetic field free for high frequencies). This reduces the internal inductance with frequency.
- For rectangular cross section with length b, width w and height h and a circular cross section conductor:
- The internal inductance at DC is about 20…40% of the self inductance. At very high frequencies the internal inductance diminishes, so the self inductance remains about 60…80% of the DC value.
- Note, that German literature often talks about “Selbstinduktivität”, when they really mean loop inductance (e.g. in case for inductance formulas of coax cable, double conductor in free space, or single conductor above ground plane configurations).
L_11 equiv L_"self"=L_"int" + L_"ext"
L_"int,rect" = {%mu% cdot b cdot w} over {12 cdot h} approx {{w} over {h}} cdot 1 "nH/cm" " " L_"int,circ"={%mu% cdot b} over {8 %pi%} = 0.5"nH/cm"

---
EM theory basics I – Inductance confusion III
- Multiple descriptions exist for a given physical setup. Three conductor physical setup (left) showing self inductance Lii and mutual inductance Lij. Loop inductance representations with ideal reference conductor (right) showing the loop inductance
  Lii− Li0−L0i+ L00 and the loop mutual inductance Lij− Li0−L0j+ L00
- The right model requires I0+I1+I2=0. For details see “Simulating the W element” in the Intranet HF &Transponder competence center's PDF archive.
V
+ ‒
L11
L12·dI2/dt+L10·dI0/dt
I1
V
L22
L21·dI1/dt+L20·dI0/dt
I2
V
L00
L01·dI1/dt+L02·dI2/dt
I0
+ ‒
+ ‒
V
L22−L20−L02+L00
(L21−L20−L01+L00)·dI1/dt
I2
I0=−I1−I2
V
I1
L11−L10−L01+L00
+ ‒
+ ‒
(L12−L10−L02+L00)·dI2/dt

---
EM theory basics II – High frequency effects I
Every piece of conductor has parasitic effects. Rules of thumb:
  1. coax cable & 50Ω track: 1pF/cm capacitance,
     narrow track & twisted pair cable: 0.5pF/cm,
  2. coax cable & 50Ω track: 2.5nH/cm loop inductance,
     twisted pair & narrow track: 10nH/cm loop inductance,
  3. track/cable introduces 50ps/cm signal delay,
  4. self-inductance decreases somewhat with frequency, resistance rises significantly with frequency (complex skin effect):
- RLC elements exist to neighbor structures, too.
- Physical R/L/C components all have frequency-, temperature- and voltage-dependent RLC equivalent circuits and self-resonance.
  1. 0805 capacitors have typically 1.5nH self inductance and 0.15Ω resistance,
  2. 0805 pads have 0.2pF capacitance to ground (relevant for capacitors < 10pF).
  3. See also Practical issues XII – Tolerances and aging.
Z(f)=Z_"DC" + z cdot sqrt{f}

---
EM theory basics II – High frequency effects II
Skin effect and skin depth as a mathematical aid
  1. Skin depth is wih ρ: specific resistance and μ: permeability
  2. For 35µm copper tracks no skin effect up to 15MHz (µr=1, ρCu=1.8e-8Ωm).
  3. 10mil (0.25mm) track centered 0.32mm (12.6mil) above a 100mm (4”) wide ground plane (both layers 35µm thick): loop resistance (including ground plane resistance – however, this is still below 1mΩ/cm @ 1GHz) and loop inductance:
    1. RDC=20mΩ/cm, R100MHz=76.4mΩ/cm, R1GHz=255mΩ/cm
    2. LDC=10.94nH/cm, L100MHz=6.15nH/cm, L1GHz=6.06nH/cm
  4. 0.14mm2 cross section (AWG26) copper twisted pair cable in free space (loop resistance and loop inductance). Skin effect occurs here above 100kHz (!):
    1. RDC=2.6mΩ/cm, R100MHz=53.4mΩ/cm, R1GHz=111.5mΩ/cm
    2. LDC=6.35nH/cm, L100MHz=5.10nH/cm, L1GHz=5.04nH/cm
%delta%(f) = sqrt{ {%rho%} over {%pi% cdot f cdot %mu% } }

---
EM theory basics II – High frequency effects III
- 10mil (0.25mm) wide and 35µm thick conductor 0.32mm above ground plane. Magnetic flux |B| at DC, 10MHz and 100MHz and current density |J| at 100MHz. A magnetic field concentration can be observed with rising frequency.
- Note, that the skin effect for the ground plane means, that the return current is concentrated below the conductor.
|B| @ DC
|B| @ 10MHz
|J| @ 100MHz
|B| @ 100MHz
conductor
ground plane

---
EM theory basics II – High frequency effects IV
- 10mil (0.25mm) wide and 35µm thick conductor above 4” (100mm) wide ground plane loop inductance frequency dependance for different insulator thickness.
- Per unit length loop inductance reduction is due to field concentration around the conductor at high frequencies.
- Textbook loop inductance formulas are given for the DC case.
Frequency / Hz
Loop inductance / nH/cm

---
EM theory basics II – High frequency effects VI
Characteristic impedance
  1. Every trace/cable has a geometry dependent characteristic impedance, at which no reflection occurs, if terminated accordingly at both ends.
     L' is the per unit length loop inductance, C' is the per unit
     length capacitance.
  2. This impedance is not a physical resistance by means of thermal noise and signal damping. That is, a lossless/noiseless superconducting cable and free space also have a meaningful characteristic impedance. For example, free space has
Radiation – from Maxwell's equations: if it is not DC, it is radiating.
  1. Power loss into free space: KCL and KVL (Kirchhoff I-II) and Ohm's Law not valid any more – derived for stationary current fields, may be used with caution only.
  2. Radiation especially occurs at 90° corners a.k.a. kinks (a via is a kink, too) and at special geometries, such as stubs, slots and patches.
  3. Antenna structures work identically in both directions (transmitting and receiving).
Z_0 = sqrt{{L'} over {C'}}
Z_0 = sqrt{{%mu_0%} over {`%varepsilon_0%}} = 377 %OMEGA% equiv E over H

---
EM theory basics II – High frequency effects VII
Distributed effects I
  1. At high frequency the voltage along a track is not identical for different places due to finite wave propagation speed. KCL, KVL and Ohm's Law not valid again.
  2. Wave propagation speed is about 0.48∙c on PCB mid layers and about 0.65∙c in coax cables and PCB top/bottom layers.
  3. Distributed effects are noticeable, if geometry size in propagation direction > λ/10.
  4. Distributed effects are λ/2 periodic. At a given frequency (i.e. sinusoidal signal), a (lossless) track with length x behaves the same as a track with length x+λ/2.
  5. Some characteristic effects occur at λ/8, λ/4 and λ/2 geometries.
  6. Identical definitions exist. Example: f=1GHz, coax cable length=5.3cm, εr=2. Propagation wavelength calculates to λ=v/f=21.2cm. “cable length is λ/4 at 1GHz” or “cable length is 90° at 1GHz”.
v = {c} over {sqrt {` %mu_"r"% cdot %varepsilon_"r"%} }

---
EM theory basics II – High frequency effects VIII
Distributed effects II
  1. Reflections occur at every place, where the characteristic impedance changes abruptly: incorrect terminations, kinks (including vias), track width changes (including track endings at large copper planes), ground plane/neighborhood inhomogeneities.
  2. Reflections perform impedance transformations, may be intentionally utilized by λ/8, λ/4 and λ/2 geometries.
  3. Resonances are likely to occur at λ/4 and λ/2 geometries (tracks have Q≈10..20).
  4. Standing waves are caused by reflections at λ/2 geometries (especially k∙λ/2, where k>1). In this case, the envelope of the wave is a low-frequency sinus, that is not time-dependent.
  5. Note: formulas usually assume transverse electromagnetic (TEM) waves. As material properties are frequency dependent, a dispersive wave occurs with small longitudinal E and H field components, called quasi-TEM wave. However, TEM equations are usually good approximations for up to some GHz.

---
EM theory basics III – Radiation I
- Every piece of conductor and each component is radiating, if it is exposed to AC voltage/current (see Maxwell's equations). The only question is: how much?
- A radiating element is called antenna.
- Usually three geometrical zones of an antenna radiation are distinguished:
  1. Reactive near field: for distances d < λ/(2π) from the antenna. The electromagnetic coupling to a victim conductor (receiving antenna) can be modeled by lumped capacitor/inductor elements.
  2. Radiated far field: for distances d > 2λ from the antenna. In this region the radiation source is considered as a singularity in space and the magnitude of the electromagnetic field is proportional to d−2
  3. Radiated near field: for distances λ/(2π) < d < 2λ. In this region the magnitude of the electromagnetic field is proportional to d−1
Upon geometry, two antenna types are discussed, depending on the EM wave component dominating the reactive near field:
  1. Magnetic antenna: a conducted current is flowing in the antenna, e.g. loop antenna.
  2. Electric antenna: the current loop is closed across a dielectric, e.g. dipole antenna.

---
EM theory basics III – Radiation II
- Antenna efficiency (radiated power/incident power) is maximum for 180° electrical length. This usually means λ/2 geometry size, e.g. for a loop antenna. However, for antennas utilizing reflections/mirroring, this means λ/4 geometry size, e.g. for rod antennas or grounded patch antennas or harness connected to car battery.
- Remember, that RF equations are λ/2 periodic! A loop antenna with a circumference of λ/2 is only more efficient than a loop antenna with λ circumference due to the reduced ohmic resistance of the shorter conductor.
- We're interested in the frequency range of 100kHz to 1GHz, that is for a free space wavelength in the range of 3000m...30cm. In this range we have two effective antennas:
  1. PCB tracks achieve λ/2 or λ/4 electrical length for frequencies above 200MHz: for example for v=0.7∙c and 200MHz: λ/4=26.3cm λ/2=52.5cm
  2. Typical harnesses have λ/2 or λ/4 electrical length for frequencies below 100MHz: for example for 1.5m harness and v=0.7∙c: λ/4 @ 35MHz and λ/2 @ 70MHz
  3. In both cases, consider harmonics.

---
EM theory basics III – Radiation III
- Radiated emissions are measured usually with 1m or 3m distance from the DUT/harness.
- This means, that a radiated measurement shows no differential mode emissions, but only common mode emissions of the harness. As the incident and the return current flows in two conductors separated only a few mm apart, the differential mode electromagnetic field is canceled at the measuring antenna.

---
Control theory basics I − Transfer function I
- Here we are interested in the subset of single-input single-output (SISO) linear time-invariant (LTI) stable systems without dead time only (“well behaved” systems).
- Any system can be described in time domain and frequency domain equivalently. Transformation between the domains is made by the Laplace transformation
- As the Laplace integral is tedious to solve (especially the inverse one), use a time/frequency domain table for common building blocks (out of scope here).
- A system in time domain is described by differential equations, so the Laplace transformation is a convenient way to solve differential equations.
- Algebra says, that any polynom with real coefficients can be written as a product of at most second order polynoms with real coefficients:
%Ux2112
G(s)=%Ux2112 left lbrace g(t) right rbrace = int from 0 to infinity g(t)e^{-s cdot t} "d"t " with " p equiv s=%sigma% + j cdot %omega% "as the complex frequency"
g(t)=%Ux2112^{-1} left lbrace G(s) right rbrace = 1 over {j cdot 2%pi%} cdot int from c-j cdot infinity to c+j cdot infinity G(s)e^{s cdot t} "d"s "
sum from n=0 to N a_n cdot x^n = prod from i left(b_i cdot x^2 +c_i cdot x + d_i right) " for " a_N <> 0

---
Control theory basics I − Transfer function II
- Transfer functions (TF) in the frequency domain can be written as a ratio of two polynoms:
- The roots of the nominator are called zeros. The roots of the denominator are called poles.
- According to polynom decomposition, both zeros and poles are either real numbers or conjugate complex. Allowing for the zeros zi and the poles pi complex numbers:
G(s) = {sum from i=1 to n a_i cdot s^i} over {sum from i=1 to m b_i cdot s^i} " with " n<=m
G(s) = k_0 cdot {{prod from i=0 to n left( s-z_i right)} over {prod from i=1 to m left( s-p_i right)} }

---
Control theory basics I − Transfer function III
- A general SISO LTI system is composed of a plant (forward part) A(s) and a feedback part B(s). The feedback is chosen negative by definition. Positive feedback can be achieved by changing the sign of the feedback function B(s).
- The TF of this system is the TF of the closed loop:
- The TF of the open loop is by definition: H(s)=F(s)/E(s)=A(s)∙B(s)
- The denominator of G(s) is 1+A(s)∙B(s) and is called characteristic polynom and its roots (the poles of the closed feedback loop) entirely determine the stability of the system.
- Unfortunately, it is tedious to calculate the denominator roots of G(s). However, the roots of A(s) and B(s) are usually known (or are easier to determine).
- Many methods therefore focus on determining/estimating the poles of the closed loop transfer function G(s) by the knowledge of the open loop TF poles of A(s)∙B(s).
G(s) = {Y(s)} over {X(s)} = {A(s)} over {1+A(s) cdot B(s)}
A(s)
B(s)
Y(s)
X(s)
E(s)
F(s)
−

---
Control theory basics I − Transfer function IV
- The poles of the closed loop are not identical to the poles of the open loop.
- Decomposition of the A(s) and B(s) functions as a polynom ratio shows G(s) in a different light (omitting the function argument s for brevity):
- The feedback shifts poles (especially, if we have zeros in the open loop TF): the open loop characteristic polynom is dA∙dB, but in the closed loop we get a new term with the product of the open loop zeros.
- By inspecting the nominators of H and G: the feedback replaces the zeros of the feedback function by the poles of the feedback function.
"with " A = {n_"A"} over {d_"A"} " and " B = {n_"B"} over {d_"B"}
H = A cdot B = {n_"A" cdot n_"B"} over {d_"A" cdot d_"B"}
G = {A} over {1+A cdot B} = {n_"A" cdot d_"B"} over {n_"A" cdot n_"B" + d_"A" cdot d_"B"}

---
Control theory basics II − Pole zero plot I
- The poles and zeros can be plotted graphically on the complex (angular) frequency plane. A typical plot shows zeros (circles) and poles (crosses) in the left half plane (LHP). A pole-zero plot with k0 completely describes a SISO LTI system without dead time.
- Such a system is stable if and only if: all poles are lying in the LHP
- Such a system is unstable if: there are poles in the right half plane (RHP) or there is a multiple pole at the origin (s=0).
- Such a system is at its stability boundary if there are single poles at σ=0.
- Such a system has minimal phase, if all zeros are in the LHP. The system has nonminimal phase, if some zeros are in the RHP (e.g. SEPIC converter).
- The quality factor of a conjugate complex pole is p=σp+j∙ωp given as: Qp=|ωp|/|p|
j∙ω
σ
LHP

---
Control theory basics II − Pole zero plot II
- Low frequency (dominating) poles and zeros are close to the σ=0 axis.
- High frequency poles and zeros lie towards the left end.
- The TF is a complex function describing magnitude and phase.
- A LHP pole decreases the phase (more negative).
- A LHP zero increases the phase.
- Attention: a RHP zero decreases the phase.
- Negative feedback shifts the phase by 180°.
- The stability boundary is given for |G(s)|=1 and phase(G(s))=0°=−360°
- Accounting for the negative feedback, the maximum allowed phase shift of the open loop is −180° if stability is required.
- If a conjugate complex pole is dominating, the ringing is getting more severe with increasing Qp. Considering the step answer and allowing for 4.3% overshoot, Qp<0.7 is required (that is, for equally scaled σ and j∙ω axis, less than 45° angle from the σ axis).

---
Control theory basics III − Bode plot I
- The Bode plot shows the magnitude (in dB) and the phase of a transfer function.
- The closed loop is unconditionally stable if and only if the Bode plot of the open loop features all of the following:
  1. gain margin (the magnitude is below 0dB @ phase=−180°)
  2. phase margin (the phase is above −180° @ magnitude=0dB)
  3. the magnitude crosses the 0dB point with −20dB/decade slope
  4. all the Bode plot “wisdom” is valid only for minimal phase systems
- The last two conditions are often ignored with catastrophic consequences. If the slope at the 0dB point is −40dB/decade, the ringing of the closed loop can be much severe, than estimated from the phase margin of the open loop's Bode plot.
- Construction rules for the Bode plot:
  1. a LHP pole adds −20dB/decade to the magnitude slope and −90° to the phase
  2. a LHP (RHP) zero adds 20dB/decade to the magnitude slope and 90° (−90°) to the phase. The RHP zero adds overall 180° phase additionally.
  3. a LHP conjugate complex pole adds a peak (height depending on Q) and −40dB/decade to the magnitude slope and −180° to the phase

---
Control theory basics III − Bode plot II
- The Bode plot shows, that with rising gain k0 the stability worsens.
- What if the magnitude does not cross the 0dB point with −20dB/decade slope?
  Solution: use the root locus plot (or numerically compute the closed loop TF / Bode plot).
|G(s)|dB
k0
ω
ω
|G(s)|dB
ω
k0
ω
phase
−45°
−90°
−135°
−180°
phase
margin
gain
margin
−20dB/dec

---
Control theory basics III − Bode plot III
- For real poles and zeros the frequencies in the pole zero plot are identical of the kink frequencies in the Bode plot.
- Normalized PT2 transfer function with conjugate complex poles:
- The unity gain frequency where
  −90° phase shift occurs is:
- The damping coefficient is:
- Conjugate complex poles occur for D < 1. Peaking occurs for
- Real and imaginary parts of the poles are:
- Peaking frequency is:
- Ringing frequency in time domain (step answer) is ωr. The exponential decay constant is ωt∙D:
G(s)=1 over {%tau%_2^2 cdot s^2 + %tau%_1 cdot s +1}
%omega%_"t" =1 over {%tau%_2}
D ={%tau%_2} over {2%tau%_1}
D < sqrt{2}
alignl Re(s_"p")=-%omega%_"t" cdot D ~~ Im(s_"p")=+-%omega%_"t" cdot sqrt{1-D^2}
%omega%_"r" =%omega%_"t" cdot sqrt{1-D^2} = im(s_"p")
y(t) ` prop ` e^{-%omega%_"t" cdot D cdot t} cdot sin left(%omega%_"r" cdot t + %phi% right)

---
Control theory basics III − Bode plot IV
- Correspondence between pole zero plot (left), Bode plot (right) and transient step response (bottom). Figures for illustration only, not to scale.
- Damping coefficient D can be determined graphically: D=cos(α)
ωr
ωt
−40dB/dec
ω
|G(s)|
ω
−90°
−180°
0dB
Phase
{2%pi%} over {%omega%_"r"}
t
y(t)
1
%omega%_"t" cdot D %omega%_"r"=%omega%_"t" cdot sqrt{1-D^2}
j∙ω
σ
α

---
Control theory basics IV − Root locus plot I
- The root locus plot is a pole zero plot showing the poles and zeros of the open loop.
- Segments show the position of the poles of the closed loop as a function of k0
- Elementary construction rules:
  1. the root locus plot is symmetrical to the real (σ) axis,
  2. the poles of the closed loop start at the poles of the open loop for k0=0. n poles end at open loop zeros for k0→∞. n−m poles end in infinity. The asymptotes are separated equally, that is with 360°/(n−m) spacing.
  3. a point on the real axis is part of the root locus, if there is an uneven number of total poles+zeros on the axis right from the point (don't count conjugate complex poles/zeros).
Use a mathematical software tool like Matlab or Scilab to plot the root locus and get the frequency and critical gain values by clicking on the diagram.
  1. For Scilab use the evans() and krac2() functions for root locus plots and critical gain determination, respectively.

---
Control theory basics IV − Root locus plot II
3 problematic cases: a) second order lowpass plant A(s) with two real poles p1 and p2 and full feedback B(s)=1. As the open loop features real poles only, no ringing is expected. However, above a critical OpAmp DC gain kc, the closed loop shows conjugate complex poles and ringing occurs for a step input.
  1. The critical frequency pc is given as:
  2. The critical gain kc is given as:
  3. Numerical example with p1=−10Hz, p2=−10MHz:
     pc≈−5MHz, kc≈2.5∙105=108dB
     Q=0.7 for kc=114dB
  4. Numerical example with p1=−10Hz, p2=−10kHz:
     pc=−5005Hz, kc=249.5=48dB
     Q=0.7 for kc=499.5=54dB
  5. Note: the closer the poles of the open loop to each other, the less gain is required to achieve conjugate complex poles for the closed loop.
p_"c"=-0.5 cdot {left lline p_1 + p_2 right rline}
k_"c"= left lline left(p_"c" / p_1 -1 right) cdot left(p_"c" / p_2 -1 right) right rline
j∙ω
σ
p1
p2
pc

---
Control theory basics IV − Root locus plot III
- b) a dominant conjugate complex poles and a high frequency pole. With full feedback above critical gain the conjugate complex poles appear on the RHP and the closed loop finally gets unstable (left).
- c) 3 real poles are potentially unstable (middle). “Well placed” zeros inhibit conjugate complex poles (from middle to right picture) and improve system bandwidth.
j∙ω
σ
j∙ω
σ
j∙ω
σ

---
Control theory basics V − Rules of thumb
- High gain k0 is required for minimum steady state error of the step response of a plant without integrator. High gain k0 reduces phase margin and can create instability. Chose the gain carefully (tolerances!) for a P (proportional) regulator (typical OpAmp circuits with resistive divider feedback).
- Partial feedback (e.g. resistive divider) helps for stability.
- An open loop zero left from the dominant pole (higher frequency) solves a large amount of stability problems.
- Lowpass feedback shifts poles (may become unstable), but simultaneously adds a zero.
- Aperiodic step response requires ≥80° phase margin. The amount of ringing below 40° phase margin is usually not accepted.
- A PD (proportional-differentiating) regulator is fast, but it amplifies noise.
- A PI (proportional-integrating) regulator has zero steady state error, but it is slow.
- A PID regulator with optimum coefficients (coefficient determination is out of scope here, see e.g. Ziegler-Nichols) combines the advantages of a PD and a PI regulator. A PID regulator with bad coefficients combines the disadvantages of a PD and a PI regulator.
- The more complex the regulator, the harder to find “good” coefficients over parameter drift due to tolerances, temperature drift, etc.

---
Practical issues I – What frequencies do I have? I
- The obvious ones: input/output signal frequencies, quartz & IC clock frequencies (don't forget neither the charge pump and switched-capacitor amplifier nor ADC/DAC clocks).
- The semi-obvious ones: signal/clock harmonics.
- The non-obvious ones I: nonlinear elements (e.g. diodes, transistors, varistors) generate intermodulation frequencies of clock (incl. harmonics) and I/O signal (incl. harmonics):
- f=a·fCLK + b·fsignal with a, b integer numbers (may be negative, too). For the sum |a|+|b| is called intermodulation order (usually only for a≠0, b≠0 to distinguish from harmonics).
  1. Third order intermodulation frequencies (products) are:
     ±2·fCLK ± 1·fsignal and ±1·fCLK ± 2·fsignal (4 positive and 4 negative frequencies)
The non-obvious ones II: broadband external noise (from neighbor PC, DC/DC converter, electrical machines, aerial broadcast, etc.) and local thermal noise.

---
Practical issues I – What frequencies do I have? II
Intermodulation at a diode. Two small sinusiodal input voltages with 100kHz and 110kHz. The current is rectified and the envelope is not sinusoidal. Nonlinearity increases with voltage amplitude.
Relative input voltage
Time / ms
Relative current
V≈
I
Vin/VT=cos(100kHz∙2π∙t)
      +cos(110kHz∙2π∙t)
I/I0=exp(Vin/VT)−1
Vin
I

---
Practical issues I – What frequencies do I have? III
The current spectrum is from DC to infinity with 110kHz−100kHz=10kHz spacing. The plot is normalized to have 0dB at the input frequencies of 100kHz and 110kHz, respectively.
Frequency bins / kHz
Relative current level / dB
2nd harmonics
3rd harmonics
4th harmonics
DC & IM1
IM2
IM3
IM4
IM5
IM6
IM7