Design Flow Overview
Design Chip Core
Extract Unused IOs
Define Reconf. Module
Develop Ex. Apps.
Develop Cell Library
Coarse Grain Mapping
Merge
Generate Reconf. Module
CPU
C
P
InterConnect
[Speaker Notes: Define application class, design parent module (e.g. chip core, at least entities) except reconf.module Automatically extract unused signals → reconf. signals Define signal usage: dynamic (to interconnect), direct (Clk, Reset), parametrized, configured, constant Dynamic signals: define connection type, e.g. Bit, Byte, Word → individual tree in interconnect Define Reconf.Module Use reconf.signals, define config and param interface Develop Example Applications Select IOs, set parametrized signals, auto-generate module, testbench and firmware templates, manual development and verification (Iteratively) Develop Cell Library & Coarse Grain Mapping Cell: Select IOs, auto-generate module and testbench templates, manual develop-ment and verification, develop variants (incl. automatic equivalence checking) Automatically extract and map ex.apps., verify results (simulation, equiv. checking) Automatically generate Interconnect and Reconf.Module Oversizing Verify (simulation, equivalence checking) using auto-generated wrappers and bitstreams → IP Core, auto-generated instantiation in chip core Verify with slightly modified testbenches Post-Silicon Phase: Ex.Apps: use generated bitstream; New Apps: identical flow except no Cell Library development and Merge is merely a mapping]

---
Design Flow Automation
Please see the Notes.
[Speaker Notes: • manual: design parent module (e.g. chip core) → not specific • automatic: identify unused pins → define as reconf.signals • manual: specify usage, conn.type → add information by user ◦ automatic: check consistency • manual: specify config & param interface → add information by user ◦ supports user by pre-defined interfaces, e.g. to CPU (OpenMSP430) • manual: specify ex.app: select IOs ◦ automatic: sanity check available signals • automatic: generate template module, testbench and firmware ◦ ports ◦ testbench: instantiation, checks for constant output signals, set values of constant input signals ◦ firmware: initialization function to download configuration data and set parameters, define constants • manual: develop example application module, testbench, verify → add information by user ◦ pro: use Verilog, a widespread HDL, not something custom → verification: wide-spread tools; test with real sensors on FPGA • manual: develop driver and firmware for each ex.app → add information by user ◦ driver: ex.app specific functions: set/query parameters, enable/disable, ... ◦ use init function and constants from auto-generated files ◦ firmware for WSN SoC using the Ex.App. • manual: iterative definition/refinement of cells and small adaptions to ex.apps. ◦ identify common structures in ex.apps. (e.g. counters, arithmetic operations, ...) → candidates for cells ◦ minor coarse-grain synthesis specific adaptions of ex.apps (e.g. width of constant values) ◦ here comes the developers intelligence • manual: specify cell: IOs and their conn.type → add information by user • automatic: generate template module and testbench ◦ ports ◦ testbench: instantiation • manual: develop cell, testbench, verify, add reduced and topographical variants → add information by user • automatic: equivalence checking of variants • automatic: extraction and mapping of ex.apps. • automatic: FSM extraction, replace by TR-FSM • automatic: check that all ex.apps are mapped to netlists only instantiating cells • automatic: generation of netlist and bitstreams for verification using simulation and equivalence checking • manual: specify oversizing rules → add information by user • automatic: merge ◦ select number of required cell instances, apply oversizing rules, optimize interconnect ◦ generate Verilog module ◦ generate bitstreams for each ex.app (used by simulation, equivalence checking, firmware) ◦ generate wrappers for all ex.apps for verification using simulation and equivalence checking • automatic: generate reconf.module ◦ add config and param interface ◦ generate wrappers for all ex.apps for verification using simulation and equivalence checking • manual: verify parent module (including CPU) with firmware ◦ use auto-generated testbench template ◦ copy-paste testbench processes from ex.apps, customize external modules ◦ use manually developed firmware which includes auto-generated bitstreams and initialization routines ◦ use auto-generate simulation initialization (load firmware to Flash) • manual: specify top-level chip module (pad cells) → add information by user • automatic: create top-level chip module ◦ instantiate pad cells (for chip synthesis) or use (mostly) direct connections (for FPGA tests) ◦ handle vector ports ◦ handle bidirectional and open drain ports • manual: verify top-level chip module with simulation ◦ manually create testbench (future work: auto-generate testbench template with component and instanti- ation of top-level chip module) ◦ copy-paste testbench processes from ex.apps, customize external modules ◦ use manually developed firmware which includes auto-generated bitstreams and initialization routines ◦ use auto-generate simulation initialization (load firmware to Flash)]