# Chapter
## Drag Coefficient (1.1)
The force ( F ) of the wind blowing against a building is given by F = C_D %rho U^2 A / 2 , where U is the wind speed, %rho is density of the air, A the cross-sectional area of the building, and C_D is a constant termed the drag coefficient. Determine the dimension of the drag coefficient.

F left[ MLT^{-2} right] = C_D %rho left[ ML^{-3} right] left( U left[ L T^{-1} right] right)^2 {A left[ L^2 right]} over 2 ~ rightarrow ~ C_D left[ unitless right]
## Derivatives (1.7)
If u is a velocity, x a length, and t a time, what are the dimension (in MLT system) of
a) {partial u} over { partial t} , b) {{partial}^{2} u} over {partial x partial t} and c) int {{partial u} over { partial t}} dx ?

a) {partial u left[ L T^{-1} right]} over { partial t left[ T right]} rightarrow left[ L T^{-2} right] , b) {{partial}^{2} u left[ L T^{-1} right]} over {partial x left[ L right] partial t left[ T right]} rightarrow left[ T^{-2}right] , c) int {{partial u left[ L T^{-1} right] } over { partial t left[ T right] }} dx left[ L right] rightarrow left[ L^2 T^{-2} right]
## Dimensionality (1.12)
If U is a velocity, determine the dimensions of Z , %alpha and G , which appear in the dimensionally homogeneous equation: U = Z left( %alpha - 1 right) + G

%alpha and 1.0 are unit-less therefore Z has to be LT-1 as U and G has to have the same LT-1 unit.
## Tire pressure (1.48 – SI)
Carry out the previous calculations in SI units. Use the following values: volume V = 0.085 left[ m^3 right] , gauge pressure p_gauge = 179 left[ kPa right] , temperature T = 21 left[ C lsup{o} right] . atmospheric pressure p_atm = 101 left[ kPa right] , ideal gas constant R = 289.6 J kg^{-1}~{K lsup {o}}^{-1} , gravitational acceleration g = 9.81 m s^{-2} . Temperature conversions: 0 C lsup { o } = 273.15 K lsup { o } .

Ideal gas law: %rho = p over { R T } ~ rightarrow ~ %rho = { 179 left[ kPa right] + 101 left[ kPa right] } over { 289.6 left[ J over {kg {K}lsup{o}} right] 294.15 {K}lsup{o}} = 3.287 left[ {kg} over {m^{3}} right]
The weight of the air is: W = %rho g V = 3.287 left[ kg over {m^3} right] 9.81 left[ {m} over {s^2} right] 0.085 left[ m^3 right] = 2.741 left[ N right]
## Tire pressure (1.48)
A tire having a volume V = 3 left[ ft^3 right] contains air at a gage pressure of p_gauge = 26 left[ psi right] and a temperature T = 70 left[ F lsup{o} right] . The atmospheric pressure is p_atm = 14.7 left[ psi right] . The ideal gas constant is R = 1716 { ft lb_f} over {slug {R}lsup{o}} . The gravitational acceleration is g = 32.2 ft s^{-2} . Temperature conversions: 0 F lsup { o } = 459.67 R lsup { o } . Determine the density of the air and the weight of the air contained in the tire using the ideal gas law %rho = {RT} over {p} .

Ideal gas law: %rho = p over { R T } ~ rightarrow ~ %rho ={left( 26 left[ psi right] + 14.7 left[ psi right] right) 144left[ {{"in."}^2 over {ft^2}} right] }over { {1716left[ { ft lbf } over {slug {R}lsup{o}} right]} 529.67 left[ {R}lsup{o} right] } = 6.448 times 10^{-3} left[ {slug} over { ft^3} right]
The weight of the air is W = %rho g V = 6.448 times 10^{ -3 } left[ slug over {ft^3} right] 32.2 left[ {ft} over {s^2} right] 3 left[ ft^3 right] = 0.6229 left[ lb_f right]
## Flat Plates (1.75)
Two flat plates are oriented parallel above a fixed lower plate as shown in figure below. The top plate, located a distance b above the fixed plate, is pulled along with speed V . The other thin plate is located a distance cb , where 0 < c < 1.0 , above the fixed plate. This plate moves with speed V_1 , which is determined by the viscous shear forces imposed on it by the fluids on its top and bottom. The fluid on the top is twice as viscous as that on the bottom. Plot the ratio V_1 / V as a function of c .

%DELTA u_1 = V_1 , %DELTA u_2 = V - V_1 , {%tau}_1 = %mu {V_1} over { cb } , {%tau}_2 = 2 %mu {V - V_1} over { b - cb }
{%tau}_1 = {%tau}_2 rightarrow %mu { V_1} over {cb} = 2 %mu { V - V_1} over { b - cb } rightarrow V_1 left( b - cb right) = 2 left( V - V_1 right){cb}
b V_1 - cb V_1 = 2 cb V - 2 cb V_1 rightarrow b V_1 + cb V_1 = 2 cb V rightarrow V_1 over V = { 2c } over { 1 + c}
## Lubricated shaft (1.78)
AA 25-mm-diameter shaft is pulled through a cylindrical bearing as shown in figure below. The lubricant that fills the 0.3 mm gap between the shafts and bearing is an oil having a kinematic viscosity ( %nu = %mu over %rho ) of 8.0 × 10-4 m2 s-1 and a specific gravity SG of 0.91. The density of the water is %rho_{H_2 O} = 1000 kg m^{-3} .
a) Calculate the shearing stress %tau = %mu {du} over {dy} = %nu %rho {du} over {dy} between the bearing and the shaft.
b) Determine the force F = %tau A required to pull the shaft at a velocity of 3 m s-1.

The velocity difference ( du ) between the bearing and the shaft is 3 m s-1 resulting in linearly changing velocity over the 0.3 mm gap ( dy ). Therefore shearing stress left( %tau = %mu {du} over {dy} right) = %nu %rho {du} over {dy} is equal to %tau = 8.0 times 10^{-4} left[ m^2 s^{-1} right] 0.91 times 10^3 left[ kg m^{-3} right] {3 left[ m s^{-1} right] } over { 3 times 10^{-4} left[ m right] } rightarrow %tau = 7280 left[ kg m^{-1} s^{-2} right] acting on the shaft's surface  = 3.14 × 0.025 m × 0.5 m = 0.03925 m2.
Therefore F = %tau A  = 7280 kg m-1 s-2 × 0.03925 m2 = 286 N
## Water Layer (1.81)
A layer of water flows down an inclined surface with the velocity profile shown in figure below. Determine the magnitude and direction of the shearing stress that the water exerts on fixed surface for U  = 2 m s-1 and h  = 0.1 m.

{%tau} = %mu { du} over { dy} rightarrow %tau = %mu U {d left( 2 y over h - {y^2} over { h^2} right)} over { dy} rightarrow %tau = %mu {2 U} over {h} left( 1 - y over h right)
U = 2 left[ m s^{-1} right]; h = 0.1 m rightarrow %tau = %mu {2 times 2 left[ m s^{-1} right] } over { 0.1 left[ m right]} left( 1 - y over { 0.1 left[ m right]} right)
%tau = 40 left[ s^{-1} right] %mu left( 1 - y over { 0.1 left[ m right]} right) rightarrow {%tau}_{max} = 40 left[ s^{-1} right] %mu @ y = 0
## Thin Glycerin Layer (1.82)
A thin layer of glycerin ( %gamma  = 78.72 [lb/ft3] and %mu  = 0.0295 [lb s/ft2]) flows down an inclined, wide plate with the velocity distribution shown in figure below. For h  = 0.3 in. and %alpha  = 20°, determine the surface velocity, U . Note that for equilibrium, the component of weight acting parallel to the plate surface must be balanced by the shearing force developed along the plate surface. In your analysis assume a unit width.

dV = h dA ; F_1 = %gamma dV sin %alpha ; F_2 = %tau dA ;
F_1 = F_2 rightarrow %gamma dV sin %alpha = {%tau}_{bottom} dA rightarrow {%tau}_{bottom} = %gamma h sin %alpha rightarrow {%tau}_{bottom} = { %gamma h sin %alpha }
%tau = %mu { du } over { dy} rightarrow %tau = %mu U {d left( 2 y over h - {y^2} over { h^2} right)} over { dy} rightarrow %tau = %mu {2 U} over {h} left( 1 - y over h right) ; {%tau}_{bottom} = %mu {2 U} over {h} @ y = 0
{ %rho h sin %alpha } = %mu {2 U} over {h} rightarrow U = { %rho h^{2} sin %alpha } over { 2 %mu } rightarrow U = { 78.72 left[ lb ft^{-3} right] left( 0.3 left[ "in" right] { 1 left[ ft right] } over {12 left[ "in" right]} right)^{2} sin 20{circle{}}} over {2 times 0.0295 left[ lb s ft^{-2} right] }
U = { 78.72 left[ ft^{-1} right] left( 0.025 left[ ft right] right)^2 sin 20{circle{}}} over {2 times 0.0295 left[ s right] } = 0.285 left[ ft s^{-1} right]
## Pivot Bearing (1.86)
A pivot bearing ( R  = 0.5 [mm]) used on the shaft of an electrical instrument is shown in figure below. An oil with a viscosity of %mu  = 0.5 [poise] fills the 0.025 [mm] gap ( %DELTA s ) between the rotating shaft and the stationary base. Determine the frictional torque on the shaft when it rotates at 5000 [rpm].

dT = r dF ; dF = %tau dA ; %tau = %mu { du } over { dy } = %mu { r %omega } over { %DELTA s} ; dA = 2 r %pi { dr } over { sin %alpha }
T = int from{r = 0} to { R} dT = int from{r = 0} to { R } r dF = int from{r = 0} to{R} r %tau dA = int from{r = 0} to{R} r %mu {r %omega} over { %DELTA s} 2 r %pi { dr } over { sin %alpha } = 2 { %pi %mu %omega } over { %DELTA s sin %alpha } int from{r = 0} to{R} r^3 dr
T = left[ 2 over 4 { %pi %mu %omega } over { %DELTA s sin %alpha} { r^4 } right]_{l = 0}^{L} = { 1 } over {2} { %pi %mu %omega } over { %DELTA s sin %alpha} R^4
%mu = 0.5 left[ g cm^{-1} s^{-1} right] ; %DELTA s = 0.025 left[ mm right] ; %omega = 5000 left[ rpm right]
T = { 1 } over {2} { %pi times 0.5 left[ g cm^{-1} s^{-1} right] 2 %pi 5000 left[ min^{-1} right] } over { 0.025 left[ mm right] sin 30} left( 0.5 left[ mm right] right)^4 = 1.29 times 10^{-4} left[ N m right]
## Circular Plate (1.89)
A 30 cm diameter circular plate is placed over a fixed bottom plate with a 3 mm gap between the two plates filled with glycerin ( %mu  = 1.412 [Pa s]) as shown in figure below. Determine the torque required to rotate the circular plate slowly at 2 rpm. Assume that the velocity distribution in the gap is linear and that the shear stress on the edge of the rotating plate is negligible.

dT = r dF ; dF = %tau dA ; %tau = %mu { du } over { dy } = %mu { r %omega } over { %DELTA s} ; dA = 2 r %pi { dr }
T = int from{r = 0} to { R} dT = int from{r = 0} to { R } r dF = int from{r = 0} to{R} r %tau dA = int from{r = 0} to{R} r %mu {r %omega} over { %DELTA s} 2 r %pi { dr } = 2 { %pi %mu %omega } over { %DELTA s } int from{r = 0} to{R} r^3 dr
T = left[ 2 over 4 { %pi %mu %omega } over { %DELTA s } { r^4 } right]_{l = 0}^{L} = { 1 } over {2} { %pi %mu %omega } over { %DELTA s } R^4
T = { 1 } over {2} { %pi 1.412 left[ Pa s right] 4 %pi left[ min^{-1} right] } over { 3 left[ mm right] } left( 15 left[ cm right] right)^4
T = 1 over 2 {%pi 1.412 left[ N m^{-2} s right] 4 %pi left[ min^{-1} right]} over { 60 left[ s min^{-1} right] 3 times 10^{-3} left[ m right]} left( 1.5 times 10^{-1} left[ m right] right)^4 = 0.078 left[ N m right]
# Chapter
## U-Tube Mercury Manometer (2.36)
A U-tube mercury manometer is connected to a closed pressurized tank as illustrated. If the air pressure is 2 psi determine the differential reading h. The specific weight of the air is negligible.

P_{air} - { %gamma }_{H_{2}O} left(h + h_{water} right) + { {%gamma}_{Hg} } h = P_{air}
SG_{Hg} {%gamma}_{H_{2}O} left( h right) = {%gamma}_{H_{2}O} left( h + h_{water} right)
13.6 h = h + 4 left[ ft right] ~ rightarrow ~ h = {4 left[ ft right]} over { 12.6} = 0.317 left[ ft right]
## Tank Compartments (2.38)
Compartments A and B of the tank shown in figure below are closed and filled with air and a liquid with a specific gravity equal to S.G.=a . Determine the manometer reading ( h [L] ), if the barometric pressure ( P_0 ) is and the pressure gage reads P_g [FL^-2] . The effect of the weight of the air is negligible.

P_g - { %gamma }_w h + { %gamma }_l h + { %gamma }_m z = P_0
P_g - P_0 + {%gamma}_m z = h left({%gamma}_w - {%gamma}_l right)
h = { P_g - P_0 + {%gamma}_m z} over { { %gamma }_w - { %gamma }_l } rightarrow h = { P_g - P_0 + z {%gamma }_w SG_{m} } over {{%gamma}_w left( 1 - SG_{l} right)}
## Cylindrical Tank (2.46)
The cylindrical tank with hemispherical ends contains a volatile liquid and its vapor. The liquid's density is {%rho}_{liquid} = 800 left[ kg m^{-3} right] , and the vapor's density is negligible. The absolute pressure in the vapor is p_{ vapor} = 120 left[ kPa right] and the absolute atmospheric pressure outside the tank is p_{0} = 101 left[ kPa right] . The gravitational acceleration is g = 9.81 left[ m s^{-2} right] . Determine:
a) the gauge pressure p_{ gauge} reading on the pressure gauge, and
b) the height, h, of the mercury ( {%rho}_{Hg} = 13,600 left[ kg m^{-3} right] ), manometer.

p_{vapor} + {%rho}_{liquid} g h_l = p_0 + p_{gauge} ~ rightarrow ~ p_{gauge} = p_{vapor} + {%rho} g h - p_0
p_{gauge} = 120 left[ kPa right] + 800 left[ kg m^{-3} right] 9.81 left[ m s^{-2} right] 1 left[ m right] - 101 left[ kPa right] = 26.85 left[ kPa right]
p_{vapor} + {%rho}_{liquid} g h_l - {%rho}_{Hg} g h = p_0 ~ rightarrow ~ h = {p_{vapor} + {%rho}_{liquid} g h_l - p_0} over { {%rho}_{Hg} g} = { p_{gauge} } over { {%rho}_{Hg} g}
h = {120 left[ kPa right] + 800 left[kg m^{-3} right] 9.81 left[ m s^{-2} right] 1 left[ m right] - 101 left[ kPa right]} over { 13,600 left[ kg m^{-3} right] 9.81 left[ m s^{-2} right]} = { 26.85 left[ kPa right] } over {13,600 left[ kg m^{-3} right] 9.81 left[ m s^{-2} right]} = 0.2012 left[ m right]
## Pressure in two pipes (2.49)
Two pipes are connected by a manometer. Determine the pressure difference, p_A - p_B between the pipes. Use the following notation for the heights: h_1 = 0.5 left[ m right] , h_2 = 0.6 left[ m right] , h_3 = 1.3 left[ m right]

p_A + {%gamma}_{water} left( h_1 + h_2 right) - {%gamma}_{gauge} h_2 + {%gamma}_{water} left( h_3 - h_1 right) = p_B
p_A - p_B = - {%gamma}_{water} left( h_1 + h_2 right) + {%gamma}_{gauge} h_2 - {%gamma}_{water} left( h_3 - h_1 right)
p_A - p_B = {%gamma}_{water} left[ - left( h_1 + h_2 right) + {SG}_{gauge} h_2 - left( h_3 - h_1 right) right]
p_A - p_B = {%gamma}_{water} left[- h_2 + {SG}_{gauge} h_2 - h_3 right]
p_A - p_B = 9810 left[ N m^{-3} right] left(- 0.6 left[ m right] + 2.6 times 0.6 - 1.3 right) = - 3332 left[ N m^{-2} right] = - 3.332 left[ kPa right]
## Concrete steps (2.80)
Concrete is poured into the forms to produce a set of steps. Determine the weight of the sandbag needed to keep the bottomless forms from lifting off the ground. The weight of the forms is 85 lb, and the specific weight of the concrete is 150 lb/ft3.

p_1 = 2 h %gamma_{ concrete } = 150 left[ lb/ft^3 right] 2 times 8 left[ italic{"in."} right] = 200 left[ lb/ft^2 right]
p_2 = h %gamma_{ concrete } = 150 left[ lb/ft^3 right] 8 left[ italic{"in."} right] = 100 left[ lb/ft^2 right]
p_1 A + p_2 A = W_{bag} + W_{form} ~ rightarrow ~ W_bag = A left(p_1 + p_2 right) - W_{ form }
## Hinge (2.82)
A structure is attached to the ocean floor. A 2-m-diameter hatch is located in an inclined wall and hinged on one edge. Determine the minimum air pressure ( p_1 ) within the container that will open the hatch. Neglect the weight of the hatch and friction in the hinge. The moment of inertia for circle is I_xc = %pi R^4 over 4 .

{overline{p}}_w = left( {h + d over 2 sin %theta} right) %gamma_water
d over 2 p_1 A = left[ { {I_{ xc }} over { left(h + d over 2 sin %theta right) cos %theta A} + d over 2 } right] {overline{p}}_w A ~ rightarrow ~p_1 = left(h + d over 2 sin %theta right) %gamma_water {{ {%pi over 4 left(d over 2 right)^4} over { left(h + d over 2 sin %theta right) cos %theta %pi left(d over 2 right)^2} + d over 2 }} over { d over 2 }
p_1 = left(h + d over 2 sin %theta right) %gamma_water left[ {d} over { 8 left(h + d over 2 sin %theta right) cos %theta } + 1 right] = %gamma_water left( {d} over { 8 cos %theta} + {h + d over 2 sin %theta } right) = 106 left[ kPa right]
## Circular Plate (2.86)
A pump supplies water under pressure to a large tank as shown. The circular-plate valve fitted in the short discharge pipe on the tank pivots about its diameter A–A and is held shut against the water pressure by a latch at B. Show that the force on the latch is independent of the supply pressure, p, and the height of the tank, h.
y_R = { I_xc } over {h A } + h

F_R = h %gamma A
F_B r = F_R left( y_R - h right) ~ rightarrow ~ F_B = { %gamma I_xc } over { r } ~ rightarrow ~ F_B = {ML^{-2}T^{-2} L^4} over { L }
## Rectangular Gate (2.88)
A rectangular gate ( H [L] ) tall and ( w [L] ) wide in the side of an open tank is held in place by the force ( F left[MLT^{-2} right] ) as indicated in figure below. The weight of the gate is negligible, and the hinge at O is frictionless. (a) Determine the water depth ( h [L] ), if the resultant hydrostatic force of the water acts ( z [L] ) above the bottom of the gate, i.e., it is collinear with the applied force ( F left[ MLT^{-2} right] ). (b) For the depth of part (a), determine the magnitude of the resultant hydrostatic force. (c) Determine the force the hinge puts on the gate under the above condition.

a) Location of the resultant force:
h - z = { I_xc } over { y_c A } + y_c and y_c = h - 1 over 2 H
h - z = { I_xc } over { left( h - 1 over 2 H right) A } + left( h - 1 over 2 H right) = { 1 over 12 w H^3 } over { left( h - 1 over 2 H right) H w } + left( h - 1 over 2 H right)
h - z = { 1 over 12 H^2 } over { h - 1 over 2 H } + left( h - 1 over 2 H right) rightarrow left( h - z right) left( h - 1 over 2 H right) = { 1 over 12 H^2 } + left( h - 1 over 2 H right)^2
h^2 - 1 over 2 h H - z h + 1 over 2 z H = { 1 over 12 H^2 } + h^2 - h H + 1 over 4 H^2
{ 1 over 2 } h H - z h + { 1 over 2} z H = { 1 over 3 } H^2 rightarrow h left( { 1 over 2 } H - z right) = { 1 over 3 } H^2 - {1 over 2} H z
b) Magnitude of the resultant force:
F_R = { %gamma }_w left( h - H right) A + 1 over { 2 } { %gamma }_w H A = { %gamma }_w left( h - 1 over 2 H right) A = { %gamma }_w left( h - 1 over 2 H right) H w
c) Force on the hinge is zero because the force applied to the gate is collinear with the resultant force.
## Triangular Gate (2.96)
A gate having the cross-section shown in figure below is w[L] wide and is hinged at C . The gate weighs F_w left[ MLT^{-2} right] , and it mass center is d [L] to the right of the plane BC . Determine the vertical reaction at A on the gate when the water level is h[L] above the base. All contact surfaces are smooth.

Forces acting on the gate are F_h = 1 over 2 %gamma h^2 w at z + 2 over 3 h ; F_v = %gamma h b w at 1 over 2 b . F_w at d and F_A at b therefore

## Triangular Gate (2.96)
A gate having the cross-section shown in figure below is w[L] wide and is hinged at C . The gate weighs F_w left[ MLT^{-2} right] , and it mass center is d [L] to the right of the plane BC . Determine the vertical reaction at A on the gate when the water level is h[L] above the base. All contact surfaces are smooth.

Forces acting on the gate are at z + 2 over 3 h ; F_v = %gamma h b w at . F_w at d and F_A at b therefore
F_A b = F_w d - F_h left( z + { 2 over 3 } h right) - F_v 1 over 2 b
F_A b = F_w d - 1 over 2 %gamma h^2 w left( z + { 2 over 3} h right) - %gamma h b w 1 over 2 b
F_A b = F_w d - %gamma h w left[ {1 over 2} h left( z + {2 over 3} h right) + { 1 over 2 } b^2 right] = F_w d - %gamma h w left[ {1 over 2} h z + {1 over 3} h^2 + { 1 over 2 } b^2 right]
F_A = { F_w d - %gamma h w left[ {1 over 2} h z + {1 over 3} h^2 + { 1 over 2 } b^2 right] } over b
## Water tank gate (2.100)
A 4 ft (1.22 m) by 3 ft (0.91 m) massless rectangular gate is used to close the end of the water tank. A 200 lbf (890 N) weight attached to the arm of the gate at a distance l from the frictionless hinge is just sufficient to keep the gate closed when the water depth is 2 ft (0.61 m), that is, when the water ( {%gamma}_{H_{2}O} = 62.4 lb_f over ft^{3} = 9.80 kN m^{-3} ) fills the semicircular lower portion of the tank. If the water were deeper, the gate would open. Determine the distance l .

p_c = %gamma {4R} over {3%pi} = 62.4 left[ lb_f over ft^{3} right] { 4 times 2 left[ ft right] } over { 3 %pi } = 52.99 left[ lb_f over {ft^2} right] , A = {R^2 %pi} over {2} ~ rightarrow ~ A = { left( 2 left[ ft right] right)^2 3.14 } over { 2 } = 6.28 left[ ft^2 right]
p_c = %gamma {4R} over {3%pi} = 9.80 left[ kN m^{-3} right] { 4 times 0.61 left[ m right] } over { 3 %pi } = 2.54 left[ kPa right] ,
F_p = p_c A ~ rightarrow ~ F_p = 52.99 left[ {lb_f} over {ft^2} right] 6.28 left[ ft^{2} right] = 332.77 left[ lb_f right]
F_p = 2.54 left[ kPa right] 0.584 left[ m^{2} right] =1.484 left[ kN right]
y_R = { I_x } over { y_c A} = { I_xc } over { y_c A} + y_c ~ rightarrow ~ y_R = { 0.1098 R^4 } over { {4R} over {3%pi} {R^2 %pi} over {2} } + {4R} over {3%pi} = left( {3} over {2} 0.1098 + 4 over {3 %pi } right) R = 1.17 left[ ft right] = 0.36 left[ m right]
l W = left( y_R + h right) F_p ~ rightarrow ~ l = left( y_R + h right) F_p over W = 3.63 left[ ft right] = 1.108 left[ m right]
## Rectangular Gate (2.102)
A rectangular gate that is 2 m wide is located in the vertical wall of a tank containing water. It is desired to have the gate open automatically when the depth of water above the top of the gate reaches 10 m. (a) At what distance d, should the frictionless horizontal shaft be located? (b) What is the magnitude of the force on the gate when it opens?

, , and

and y_2 = 1 over 2 {y_b + y_t} = 1 over 2 24 left[ m right] = 12 left[ m right]
F_1 = { left( y_b - y_t right)^2 } over { 2 } w %gamma = { left( 4 left[m right] right)^2} over 2 times 2 left[ m right] times 9.8 left[ kN m^{-3} right] = 156.8 left[ kN right]
F_2 = left( y_b - y_t right) y_t w %gamma = 4 left[m right] times 10 left[ m right] times 2 left[ m right] 9.8 left[ kN m^{-3} right] = 784 left[ kN right] , F_1 + F_2 = F_p
y_R = { y_1 F_1 + y_2 F_2 } over { F_p } = { 12.667 left[ m right] times 156.8 left[ kN right] + 7 left[ m right] times 784 left[ kN right] } over { 940.8 left[ kN right] } = 12.111 left[ m right] ~ rightarrow ~ d = 2.11 left[ m right]
## Water tank gate
Combined shape gate is holding water. Calculate the pressure force and the location of the pressure ( {%gamma}_{H_{2}O} = 9.80 kN m^{-3} ).

Rectangle	Semi Circle
	y_{ c_c } = H + h + { 4 R } over {3 %pi} = 1.11 left[ m right]
p_{c_r} = y_{c_r} %gamma = %gamma left( 1 over 2 h + H right) = 6.86 left[ kPa right]	p_{c_c} = y_{c_c} %gamma = %gamma left( H + h + {4R} over {3%pi} right) = 10.901 left[ kPa right]
A_r = 2 R h = 0.4 left[ m^2 right]	A_c = {R^2 %pi} over 2 = 0.3925 left[ m^2 right]
I_{xc_r} = 1 over 12 2R h^3 = 0.00533 left[ m^4 right]	I_{xc_c} = 0.1098 R^4 = 0.00686 left[ m^4 right]
F_{ p_r} = p_{C_r} A_r = %gamma y_{C_r} A = %gamma left(h + 2H right) Rh newline F_{ p_r} = 2.744 left[ kN right]	F_{p_c} = p_{C_c} A_c = y_{C_c} %gamma A = %gamma left(H + h + {4 R} over {3 %pi} right) { R^2 %pi } over 2 newline F_{p_c} = 4.279 left[ kN right]
matrix{ y_{R_r} # ~ = ~ # { I_{x_r} } over { y_{c_r} A_r} = { I_{xc_r} } over { y_{c_r} A_r} + y_{c_r} ## {} # ~ = ~ # {0.00533 left[ m^4 right]} over {0.7 left[ m right] * 0.4 left[ m^2 right]} + 0.7 left[ m right] ## {} # ~ = ~ # 0.719 left[ m right]}

## Parabolic Gate
Find the pressure force and the center of the pressure on a parabolic gate shown in the figure.

p left( y right) = left(h - y right) %gamma , w = a y^{ 1 over b } , dA = w dy ~ rightarrow ~ dA = a y^{1 over b} dy
matrix{ F_p # ~ = ~ # { int from { 0 } to { h } {p left( y right) dA}} ## {} # ~ = ~ # { a %gamma int from { 0 } to { h } { left(h - y right) y^{1 over b} dy}} ## {} # ~ = ~ # { a {%gamma} int from { 0 } to { h } { h y^{1 over b} - y^{{b+1} over b} dy }} ## { } # ~ = ~ # { a {%gamma} left[ b over{ b + 1} h y^{{b + 1} over b} - b over {2b + 1} y^{ {2b + 1} over {b}} right]_0^h} ## {} # ~ = ~ # { a {%gamma} {b^{2}} over { 2b^{2} + 3b + 1 } } h^{ {2b + 1} over {b}}} matrix{ y_R F_p # ~ = ~ # {int from { 0} to { h } y {p left( y right) dA}} ## {} # ~ = ~ # {a %gamma int from { 0 } to { h } { y left(h - y right) {y}^{1 over b} dy}} ## {} # ~ = ~ # {a {%gamma} int from { 0 } to { h } { h y^{{b + 1} over b} - y^{{2b + 1} over b} dy}} ## { } # ~ = ~ # {a {%gamma} left[ b over { 2b + 1} h y^{{2b + 1} over {b}} - b over {3b + 1} y^{{3b + 1} over {b}}right]_0^h} ## {} # ~ = ~ # { a %gamma {b^{2}} over { 6b^2 + 5b + 1} h^{{3b + 1} over {b}}}}
 y_R = {y_R F_p} over { F_p } = { 2 b^{2} + 3b + 1 } over { 6 b^2 + 5b + 1 } h
## Parabolic Gate
Find the a) pressure force (10pts) and b) the center of the pressure (10pts) on a parabolic gate shown in the figure.

p left( y right) = - y %gamma , w = a y^{ 1 over b } , dA = w dy ~ rightarrow ~ dA = a y^{1 over b} dy
matrix{ F_p # ~ = ~ # { int from { 0 } to { h } {p left( y right) dA}} ## {} # ~ = ~ # { a %gamma int from { 0 } to { h } { y^{{b + 1}over b} dy}} ## { } # ~ = ~ # { a {%gamma} left[ b over {2b + 1} y^{ {2b + 1} over {b}} right]_0^h} ## {} # ~ = ~ # { a {%gamma} {b} over { 2b + 1 } } h^{ {2b + 1} over {b}}} matrix{ y_R F_p # ~ = ~ # {int from { 0} to { h } y {p left( y right) dA}} ## {} # ~ = ~ # {a %gamma int from { 0 } to { h } { y^{{2b + 1} over b} dy}} ## {} # ~ = ~ # {a %gamma left[ b over {3b + 1} y^{{3b + 1} over {b}}right]_0^h} ## {} # ~ = ~ # { a %gamma {b} over { 3b + 1} h^{{3b + 1} over {b}}}} y_R = {y_R F_p} over { F_p } = { 2b + 1} over { 3b + 1 } h
## Inclined parabolic gate (2.104)
TThe inclined face AD of the tank is a plane surface containing a gate ABC, which is hinged along line BC. The shape of the gate is shown in the plan view. If the tank contains water, determine the magnitude of the force that the water exerts on the gate.

y_0 = 2 left[ ft right] + 4 left[ ft right] = 6 left[ ft right] , y_1 = 2 left[ ft right] , y = y_0 - y' , y'_0 = y_0 - y_0 = 0 left[ ft right] , y'_1 = y_0 - y_1 = 4 left[ ft right]
y' = 4 left[ ft^-1 right] x'^2 ~ rightarrow ~ x' = {sqrt{ y' times 1 left[ ft right]}} over 2
p left( y right) = y %gamma sin %theta ~ rightarrow ~ p left( y' right) = left( y_0 - y' right) %gamma sin %theta , dA = 2 x' left( y' right) dy' ~ rightarrow ~ dA = sqrt{ left( y' right) times 1 left[ ft right] } dy'
matrix{ F_p # ~ = ~ # int from { y_0 } to { y_1 } { p left( y right) dA} ## { } # ~ = ~ # int from { {y'}_0} to { {y'}_1 } { left( y_0 - y' right) %gamma sin %theta sqrt{y' times 1 left[ ft right]} dy' } ## {} # ~ = ~ # sqrt{ 1 left[ ft right]} %gamma sin %theta int from { {y'}_0} to {{y'}_1 } { y_0 { y'}^{1 over 2} - {y'}^{3 over 2} dy' } ## {} # ~ = ~ # sqrt{1 ft} %gamma sin %theta left[2 over 3 y_0 {y'}^{3 over 2} - 2 over 5 {y'}^{5 over 2} right]_{{y'}_0}^{{y'}_1} ## {} # ~ = ~ # { sqrt{1 ft} 62.4 times 0.5 left[ lb_f ft^{-3} right] lbrace{ 2 over 3 times 6 left[ ft right] left( 4 left[ ft right] right)^{3 over 2} - 2 over 5 left( 4 left[ ft right] right)^{5 over 2}} rbrace} = 599 left[ lb right]}
## Cylindrical tank (2.130)
A 3-m-diameter open cylindrical tank contains water and has a hemispherical bottom. Determine the magnitude, line of action, and direction of the force of the water on the curved bottom.

F_p = left( h %pi d^2 over 4 - 4 over 3 %pi d^3 over 8 right) %gamma_water = 485 left[ kN right]
## Cylindrical Bulge
Determine a) the resultant hydrostatic force (10pts) and center of pressure (10pts) on a L length (into the page as shown in side view) of the semi cylindrical bulge.

F_up = {%gamma} L left( h r + r^2 - {r^2 %pi} over 4 right) , F_down = {%gamma} L left( h r + r^2 + {r^2 %pi} over 4 right)
F_vR = F_down - F_up = {%gamma} L left( hr + r^2 + { r^2 %pi } over {4} - hr - r^2 + {r^2 %pi} over 4 right) = {%gamma} L left( { r^2 %pi } over 2 right)
F_hR = { %gamma } L { h + h + 2 r } over 2 2 r = 2 {%gamma} L left( h + r right) r = 2 {%gamma} L left( { hr + r^2} right)
C_v = {{%gamma} L left[ left( h + r right) 2rh +left( h + 4 over 3 r right ) { 2 r^2 } right]} over F_hR	C_h = 4 over { 3 %pi } r
## Anchored Timber (2.135)
The homogeneous L = 10 left[ m right] long timber is h = 0.15 left[ m right] by w = 0.35 left[ m right] in cross section. Determine a) the specific weight of the timber (10pts) and the tension in the rope (10pts). The specific weight of the water is {%gamma}_water = 9.8 left[ kN m^{-3} right] .

V_timber = L w h = 10 left[ m right] 0.15 left[ m right] 0.35 left[ m right] = 0.525 left[ m^3 right]
V_water = L_water w h = 8 left[ m right] 0.15 left[ m right] 0.35 left[ m right] = 0.420 left[ m^3 right]
F_B = {%gamma}_{water} V_{water} = 4.116 left[ kN right]
F_B L_water over 2 = F_G L over 2 ~ rightarrow ~ F_G = F_B L_water over L = 3.29 left[ kN right]
F_G = {%gamma}_{timber} V_{timber} ~ rightarrow ~ %gamma_timber = F_G over V_timber = 6.27 left[ kN m^{-3} right]
F_rope = F_B - F_G = 0.826 left[ kN right]
## Floating Cylinder (2.137)
A tank of cross-sectional area A is filled with a liquid of specific weight %gamma_1 as shown if figure below. Show that when a cylinder of specific weight %gamma_2 and volume is floated in the liquid, the liquid level rises by an amount .

{%gamma}_1 {%DELTA}h A = {%gamma}_2 V ~ rightarrow ~ %DELTA h = {%gamma}_2 over {%gamma}_1 V over A
## Floating Cylinder Tank (2.144)
Thin-walled, d = 1 left[ m right] diameter cylindrical tank is H = 3 left[ m right] tall and has a mass of m = 90 left[ kg right] . The closed top of the tank has a pressure gauge and the open bottom is lowered into water (density {%rho}_{wat} = 1000 left[ kg m^{-3} right] ) and held in position ( h = 0.6 left[ m right] portion sticking out from the water) by a steel block (density {%rho}_{block} = 7840 left[ kg m^{-3} right] ). Assume that the air in the tank is compressed at constant temperature ( p_atm over { {%rho}_{air} } = { p_gauge + p_atm} over { {%rho}_comp} = constant ). The atmospheric pressure is p_atm = 101.33 left[ kPa right] .
Determine:
a) the reading on the pressure gage at the top of the tank (20pts);
b) the volume of the steel block (10pts).
The first part of the problem leads to a second order equation: a x^2 + b x + c = 0 that can be solved by the following formula: x_1,2 = {-b +- sqrt{b^2 - 4ac} } over {2 a}
You can solve the second part (without completing the first part) by knowing that the height of the compressed air in the tank is h_air = 2.581 left[ m right] .

{p_atm + p_gauge} over { {%rho}_comp } = {p_atm} over { {%rho}_air } ~ rightarrow ~ { {%rho}_air } over { {%rho}_comp } = { p_atm } over { p_gauge + p_atm } ,
{%rho}_{air} V_{cyl} = {%rho}_{comp} V_{air} ~ rightarrow ~ h_air = { {%rho}_{air} } over { {%rho}_{comp} } H = { p_{atm} } over { p_{gauge} + p_{atm} } H ,
p_{gauge} = {%rho}_{wat} g left( h_{air} - h right) = {%rho}_{wat} g left( {p_atm} over {p_gauge + p_atm} H - h right) ,
left( p_{gauge} + {%rho}_{wat} g h right) left(p_gauge + p_atm right)- {p_atm} {%rho}_{wat} g H = 0 ,
p^2_gauge + p_gauge {%rho}_{water} g h + p_gauge p_atm + p_atm {%rho}_{water} g left( h - H right) = 0
p_gauge = { - {%rho}_{water} g h - p_atm +- sqrt{ left({%rho}_{water} g h + p_atm right)^2 - 4 p_atm {%rho}_{water} g left( h - H right)} } over { 2 } = 18.915 left[ kPa right]
h_air = { p_atm } over { p_gauge + p_atm } H = 2.581 left[ m right] , V_{buoy} = left( h_air - h right) {d^2} over { 4 } %pi = 1.541 left[ m^3 right]
{%rho}_{wat} g left( V_{buoy} + V_{block} right) = mg + {%rho}_{block}g V_{block} ~ rightarrow ~ { %rho }_{ wat } V_{buoy} - m =left( {%rho}_{block} - {%rho}_{wat} right) V_{block}
{V}_{block} = {{%rho}_{wat} V_{buoy} - m} over { {%rho}_{block} - {%rho}_{wat} } = 0.208 left[ m^3 right]
## Open U-tube in Motion (2.156)
The open U-tube of the figure below is partially filled with a liquid. When this device is accelerated with a horizontal acceleration, a [L T^-2] , a differential reading, h [L] , develops between the manometer legs which are spaced a distance, l [L] , apart. Determine the relationship between a , h , and l .

{partial p} over {partial z} = -%rho (a_z + g) and {partial p} over {partial x} = -%rho a_x
dp ={{partial p} over {partial x}}dx + {{partial p} over {partial z}}dz
along a line of constant pressure dp = 0 , e.g. interfaces of liquid and air:
{{partial p} over {partial x}}dx + {{partial p} over {partial z}}dz = 0 or -%rho a_x dx -%rho (a_z + g)dz = 0
dz over dx = -a_x over (a_z + g) then the slope of the liquid surface is a negative value, dz over dx = -h over l hence , -h over l = -a_x over (a_z + g) and for a_z = 0 , a_x = a we have h = al over g
## Rotating Mercury Mirror Telescope (2.163)
The largest liquid mirror telescope uses a 6-ft diameter tank of mercury rotating at 7 rpm to produce its parabolic-shaped mirror as shown on the figure. Determine the difference in elevation of the mercury ( %DELTA h ), between the edge and the center of the mirror.

%DELTA h = { {%omega}^2 r^2 } over { 2g } ~ rightarrow ~ %DELTA h = { 7 left[ rpm right] 6 left[ ft right] } over {2 times 32.4 left[ ft / s^2 right] }
## Rotating Mercury Mirror Telescope (2.163)
The largest liquid mirror telescope uses a 6-ft diameter tank of mercury rotating at 7 rpm to produce its parabolic-shaped mirror as shown on the figure. Determine the difference in elevation of the mercury ( %DELTA h ), between the edge and the center of the mirror.

%DELTA h = { {%omega}^2 r^2 } over { 2g } ~ rightarrow ~ %DELTA h = { 7 left[ rpm right] 6 left[ ft right] } over {2 times 32.4 left[ ft / s^2 right] }
# Chapter
## Variable Area Horizontal Pipe (3.3)
Water flows steadily through the variable area horizontal pipe shown in the figure below. The centerline velocity is given by U = 10(1+x) vec i ft/s , where x is in feet. Viscous effects are neglected. (a) Determine the pressure gradient, {partial p} over {partial x} (as a function of x ) needed to produce this flow. (b) If the pressure at section (1) is 50 psi , determine the pressure at (2) by (I) integration of the pressure gradient obtained in (a), (II) application of the Bernoulli equation.

a)	{partial p} over {partial x} = - %rho U { partial U } over { partial x } ~rightarrow ~ {partial p} over {partial x} = - %rho 100 left(1 + x right)
b)	int from {0} to {l} {{ partial p} over {partial x} dx} = int from {0} to {l} { - 100 %rho - 100 %rho x dx} = - 100 %rho left(l + 1 over 2 l^2 right)
p_2 = p_1 - 100 %rho left(l^2 over 2 + l right)
p_2 = 50 left[ psi right] - 100 left[ 1 over {s} right] times 1.94 left[ {slug} over {ft^3} right] 7.5 left[ ft^2 right] times 1 left[ { ft^2} over { italic{"in."}^2 } right] = 39.896 left[ psi right]
U = 10 left( 1 + x right) , U_1 = 10 left[ ft s^{-1} right] , U_2 = 10 left( 1 + l right) left[ ft s^{-1} right]
p_1 + %rho U_1^2 over 2 = p_2 + %rho U_2^2 over 2 ~ rightarrow ~ p_2 = p_1 - %rho 10^2 { l^2 + 2 l + 1^2 - 1 } over { 2 } = p_1 - %rho 100 left( l^2 over 2 + l right )
## Circular Streamlines (3.12)
Water flows around the vertical two-dimensional bend with circular streamlines and constant velocity as shown in the figure below. If the pressure is P_1 [F{L^2}] at point (1), determine the pressure at point (2), (3). [ P_2 [F{L^2}] , P_3 [F{L^2}] ]. Assume that the velocity profile is uniform as indicated.

partial over { partial n } = - {partial over { partial r }} , Re = r , a_c = r {%omega}^2 = U^2 over r
{partial p} over {partial r} - %rho { U^2 } over { Re } - %gamma {dz} over {dn} = 0 ~ rightarrow ~ { partial p } over { partial r } - %rho { U^2 } over { r } + %gamma dz over dr = 0 ;
p - %rho U^2 ln r + %gamma z = C ; p_1 - %rho U_1^2 ln r_1 + %gamma z_1 = p_2 - %rho U_2^2 ln r_2 + %gamma z_2
z_1 = 0 ~ "and" ~ z_2 = d over 2 ~ rightarrow ~ p_2 = p_1 + %rho U^2 ln left( { R + d over 2} over { R + d} right) - %rho g d over 2
z_1 = 0 ~ "and" ~ z_3 = d ~ rightarrow ~ p_3 = p_1 + %rho U^2 ln left( { R } over { R + d} right) - %rho g d
## Free Jet (3.36)
Water flows from a pressurized tank, through a 6 [in.] diameter pipe, exits from a 2 [in.] diameter nozzle, and rises 20 [ft] above the nozzle. Determine the pressure in the tank if the flow is steady, frictionless, and incompressible. (Apply the Bernoulli equation p + %rho { U^2 } over { 2 } + z %rho g = constant .)

p_1 + %rho { U_1^2 } over { 2 } + z_1 %rho g = p_2 + %rho { U_2^2 } over { 2 } + z_2 %rho g = p_3 + %rho { U_3^2 } over { 2 } + z_3 %rho g = p_4 + %rho { U_4^2 } over { 2 } + z_4 %rho g
, , , ,
, z_3 = 2 left[ ft right] , z_4 = 22 left[ ft right]
%rho { U_3^2 } over { 2 } + z_3 %rho g = z_4 %rho g ~ rightarrow ~ %rho { U_3^2 } over { 2 } = left( z_4 - z_3 right) %rho g ~ rightarrow ~ U_3 = sqrt{ 2g left( z_4 - z_3 right) } , U_2 = left( d_3 over d_2 right)^2 sqrt{ 2g left( z_4 - z_3 right) }
p_2 + %rho { U_2^2 } over { 2 } + z_2 %rho g = p_3 + %rho { U_3^2} over {2} + z_3 %rho g ~ rightarrow ~ p_2 = %rho {U_3^2 - U_2^2} over 2 + z_3 %rho g
p_1 + z_3 %rho g = p_2 + %rho { U_2^2 } over { 2 } =%rho {U_3^2} over {2} = %rho g left( z_4 - z_3 right) = 62.4 left[ lb_f ft^{-3} right] times 20 left[ ft right] =1248 left[ lb_f ft^{-2} right] = 9.533 left[ psi right]
## Confined Flows (3.44)
Water flows steadily through the large tanks in figure below. Determine the water depth, h_A [L] . Hint: Since water is incompressible, with regards to Mass Conservation, Q = Q_A = Q_B known as Continuity equation, where Q_A = {V_A}{A_A} ,and Q_B = {V_B}{A_B} . V_{A o r B} is velocity of flow, and A_{A o r B} is the cross-section area of the tubes with diameters d_A or d_B .

U_A = sqrt{ 2gh_A } And U_B = sqrt{ 2gh_B }
Q = U_A over A_A = U_B over A_B ~ rightarrow ~ U_A = U_B { A_B over A_A } ~ rightarrow ~ sqrt{ 2 g h_A } = left( { d_B } over {d_A} right)^2 sqrt{ 2 g h_B } ~ rightarrow h_A = left( d_B over d_A right)^4 h_B
## Flow through Pipe Contraction (3.52)
Water flows through the pipe contraction shown in figure below. For the given h [L] determine the flow rate as a function of the diameter of the small pipe, D [L] . Hint : Since water is incompressible, with regards to Mass Conservation, Q = Q_d = Q_D known as Continuity equation, where Q_d = {U_d}{A_d} ,and Q_D = {U_D}{A_D} . U_{d} and U_{D} are velocities of flow at two cross-sections with area A_{d} and A_{D} and diameters d or D .

p_d + %rho { U_d^2 } over { 2 } + %rho g z_d = p_D + %rho { U_D^2 } over { 2 } + %rho g z_D = p_d + %rho g h + %rho g z_D ~ rightarrow ~ %rho { U_d^2 } over { 2 } = %rho g h ~ rightarrow ~ U_d = sqrt{ 2 g h }
U_d = Q over A_d ~rightarrow Q = d^2 over 4 %pi sqrt{ 2 g h }
## Flow through Pipe Contraction (3.52)
Water flows through the pipe contraction shown in figure below. For the given h determine the flow rate as a function of the diameter of the small pipe ( D ) and/or the big pipe ( d ).

p_d + %rho { U_d^2 } over { 2 } + %rho g z_d = p_D + %rho { U_D^2 } over { 2 } + %rho g z_D = p_d + %rho g h + %rho g z_D ~ rightarrow ~ %rho { U_d^2 } over { 2 } = %rho g h ~ rightarrow ~ U_d = sqrt{ 2 g h }
U_d = Q over A_d ~rightarrow Q = d^2 over 4 %pi sqrt{ 2 g h }
## Water flow from tank (3.76)
Water flows steadily from the large open tank. If viscous effects are negligible, determine (a) the
flowrate, Q, and (b) the manometer reading, h. The specific weight of the water is %rho_water = 1000 left[ kg m^{-3} right] . The gravitational acceleration is g = 9.81 left[ m s^{-2} right] , SG_{ Hg } = 13.6

p_1 + 1 over 2 %rho_1 U_1^2 + z_1 %rho_1 g = p_2 + 1 over 2 %rho_2 U_2^2 + z_2 %rho_2 g = p_3 + 1 over 2 %rho_3 U_3^2 + z_3 %rho_3 g , %rho_1 = %rho_2 = %rho_3 = %rho_water
p_1 = p_3 = 0 left[ kPa right] , U_1 = 0 left[ m s^{-1} right] , z_1 = 4 left[ m right] , z_3 = 0 left[ m right]
z_1 g %rho_water = 1 over 2 %rho_water U_3^2 ~ rightarrow ~ U_3 = sqrt{ 2 g z_1 } = 8.86 left[ m s^{-1} right] ~ rightarrow ~ Q = U_3 %pi D^2 over 4 = 0.0696 left[ m^3 s^{-1} right]
Q = U_3 D^2 over 4 %pi = U_2 d^2 over 4 %pi ~ rightarrow ~ U_2 = U_3 D^2 over d^2 = 13.84 left[ m s^{-1} right]
z_1 g %rho_water = p_2 + 1 over 2 %rho_water U_2^2 ~ rightarrow ~ p_2 = z_1 g %rho_water - 1 over 2 %rho_water U_2^2 = - 56.46 left[ kPa right]
p_2 - h_{2m} g %rho_water + h g SG_{ Hg } %rho_water = 0 ~ rightarrow ~ h = {h_2m g rho_water - p_2} over { SG_{Hg} g %rho_water } = 0.57 left[ m right]
## Two layer Tank (3.80)
If the viscous effects are neglected and the tank is large, determine the flow rate from the tank shown in figure below. Hint: flow rate of a fluid passing through a certain cross-section is equal to the product of Velocity and Area of that cross-section.

p_1 + %rho { U_1 } over { 2 } + %rho g z_1 = p_2 + %rho { U_2 } over { 2 } + %rho g z_2
p_1 = {%rho}_{water} g h_1 + {%rho}_{oil} g h_2 = %rho g left( h_1 + SG * h_2 right) , p_2 = 0 U_1 = 0 , z_1 = z_2 = 0
{%rho}_water g left( h_1 + SG*h_2 right) = %rho { U_2^2 } over { 2 } ~ rightarrow ~ U_2 = sqrt{ 2 g left( h_1 + SG * h_2 right) }
Q = U_2 A_2 = d^2 over 4 * %pi sqrt{ 2 g left( h_1 + SG * h_2 right) }
## Flow from a Tank
Water is discharging from a tank through a convergent-divergent mouthpiece. The exit from the tank is rounded so that losses there may be neglected and the minimum diameter is D_2 = 0.05 left[ m right] . If the head in the tank above the centre-line of the mouthpiece is h = 1.83 left[ m right] . The absolute pressure at the minimum area is and the atmospheric pressure p_0 = {%gamma}_w 10 left[ m right]
a) What is the discharge?
b) What is the diameter ( D_3 ) at the exit?
c) What would the discharge be if the divergent part of the mouth piece were removed.

a)
p_0 + {%gamma}_w h = p_2 + {%rho}_w {{U_2}^2 } over {2} rightarrow U_2 = sqrt{ {2 left(p_0 - p_2 + {%gamma}_w h right)} over {%rho}_w }
{ 4 Q } over { {D_2}^2 %pi } = sqrt{{ 2 left(p_0 - p_2 + {%gamma}_w h right)} over {%rho}_w } rightarrow { Q } = {D_2}^2 %pi sqrt{{ p_0 - p_2 + {%gamma}_w h} over { 8 {%rho}_w}}
Q = left( 0.05 left[ m right] right)^2 %pi sqrt{ 9.81 left[ m s^{-2} right] { 10 left[ m right] - 2.44 left[ m right] + 1. 83 left[ m right]} over 8 }
Q = 0.0025 left[ m^2 right] %pi sqrt{ 11.51 left[ m^2 s^{-2} right]} = 0.026 left[ m^3 s right]

b)
p_1 = p_3 , p_1 + %gamma_w h = p_3 + {%rho}_w {U_3^2} over {2} ~ rightarrow ~ %gamma_w h = %rho_w { U_3^2 } over { 2 } ~ rightarrow ~ U_3 = sqrt{ 2 g h }
U_3 = Q over { A_3 } ~ rightarrow ~ A_3 = Q over { sqrt {2 g h} } ~ rightarrow ~ D_3^2 over 4 %pi = Q over { sqrt{2 g h} } ~ rightarrow ~ D_3 = sqrt{ {4Q} over{ %pi sqrt{2 g h} }} = 0.0752 left[ m right]
c)
p_1 = p_2 , p_1 + %gamma_w h = p_2 + {%rho}_w {U_2^2} over {2} ~ rightarrow ~ %gamma_w h = %rho_w { U_2^2 } over { 2 } ~ rightarrow ~ U_2 = sqrt{ 2 g h }
Q = U_2 A_2 ~ rightarrow ~ Q = {D_2^2} over {4} %pi sqrt{ 2 g h } ~ rightarrow ~ Q = 0.0118 left[ m^3 s^{-1} right]
# Chapter
## Velocity Field (4.2)
The velocity field of a flow is given by vec{ U } = left( 3 left[ 1 over s right] y + 2left[ft over s right] right) hat{ bold{i} } + left( 1 left[ 1 over s right] x - 8left[ft over s right] right) hat{ bold{j} } + 5 left[ 1 over s right] z hat{ bold{k} } , where , y and z are in feet. Determine the flow velocity at the origin ( x_0 = y_0 = z_0 = 0 left[ ft right] ) and the y axis ( x_y0 = z_y0 = 0 left[ ft right] ).

vec{ U_0 } = left( 3 y_0 + 2 right) hat{ bold{i} } + left(x_0 - 8 right) hat{ bold{j} } + 5 z_0 hat{ bold{k} } = 2 hat{ bold{i} } - 8 hat{ bold{j} } ~ rightarrow ~ lline vec{U} rline = U = sqrt{ 2^2 + 8^2 } = 8.246 left[ ft over s right]
vec{ U_y0 } = left( 3 y + 2 right) hat{ bold{i} } + left(x_y0 - 8 right) hat{ bold{j} } + 5 z_y0 hat{ bold{k} } = left( 3y + 2 right) hat{ bold{i} } - 8 hat{ bold{j} } ~ rightarrow lline vec{ U } rline = U = sqrt{ 9y^2 + 12y+68 }
## Contracting Pipe (4.32)
The fluid velocity along the x axis is changes linearly from point A to B, such that U_A = 6 left[ m s^{ -1 } right] ~ @ ~ x_A = 0 left[ m right] and . Determine the acceleration at points A, B and C assuming steady flow. (Expressing a = f left( x right) is 10 pts, calculating a_A , a_B and a_C is 10pts).

U_A = U_0 + c x_A ~ rightarrow ~ U_0 = U_A - c x_A , U_B = U_0 + c x_B ~ rightarrow ~ c = { U_B - U_A } over { x_B - x_A } ~ rightarrow ~c = 120 left[ s^{ -1 } right]

a_A = c U_0 + c^2 x_A = 720 left[ m s^{-2} right]

## Hydraulic Jump (4.34)
 hydraulic jump is a sudden change in depth of a liquid layer as it flows in an open channel. In relatively short distance the liquid depth changes from z_1 to z_2 with a corresponding velocity from U_1 = 1.2 left[ fps right] to U_2 = 0.3 left[ fps right] . Estimate the average deceleration of the liquid as it flows across the hydraulic jump. How many g = 32.2 left[ ft over s^2 right] deceleration does it represent.

a = U { partial U } over { partial s } ~ rightarrow ~ a = {U_1 + U_2} over 2 { U_2 - U_1 } over l = { U_2^2 - U_1^2 } over { 2 l } = {0.3^2 - 1.2^2} over { 2 times 0.02} left[ ft over s^2 right] = - 33.75 left[ ft over s^2 right] = - 1.048 g
## Engine Exhaust (4.40)
The speed of exhaust gasses in a car's exhaust pipe varies in time and distance because of the periodic nature of the engine's operation and the damping effect of the distance from the engine. Assume that the speed follows U = U_0 left[ 1 + a e^{bx} sin left( %omega t right) right] relationship where U_0 = 8 left[ fps right] , a = 0.05 , b = 0.2 left[ 1 over ft right] and %omega = 50 left[ rad over s right] . Calculate and plot the fluid acceleration at x = 0, 1, 2, 3, 4 ~ "and" ~ 5 left[ ft right] for 0 <= t <= %pi over { 25} left[ s right]

U = U_0 left[ 1 + ae^{bx} sin left( %omega t right) right] , a = dU over dt = U_0 a e^{ bx} %omega cos left( %omega t right)

## Flow Past a Sphere (4.46)
A fluid flows past a sphere with an upstream velocity U_0 = 40 left[ m s^{-1} right] . The speed of the velocity along the front part of the sphere is U = 3 over 2 U_0 sin %theta . Determine the streamwise and the normal components of acceleration at point A if the radius of the sphere a = 0.20 left[ m right] .

U = 3 over 2 U_0 sin %theta
a_s = U { partial U } over { partial s } = U over a { partial U } over { partial %theta } = 3 over 2 U_0 sin %theta 3 over 2a U_0 cos %theta = 9 over {8a} U_0^2 sin left( 2 %theta right) = 8862 left[ m s^{-2} right]
a_n = U^2 over a = 9 over {4a} U_0^2 sin^2 %theta = 7430 left[ m s^{-2} right]
## Curved Hose (4.48)
Water flows through the hose with increasing speed U = 10 t left[ fps right] . For t = 2 left[ s right] determine a) the component of the acceleration along the streamline, b) the component of the acceleration normal to the streamline and c) the net acceleration (magnitude and direction).

vec{ a } = a_s hat{ bold{s} } + a_n hat{ bold{n} } , a_s = dU over dt= 10 left[ ft over s^2 right] , a_n = U^2 over { Re } = { left(10 t right)^2} over {Re} = {left( 10 left[ ft over s^2 right]right)^2 left(2 left[ s right] right)^2 } over { 20 ft } = 20 left[ ft over s^2 right]
lline vec{a} rline = a = sqrt{ a_s^2 + a_n^2 } = 22.36 left[ ft over s^2 right] , %theta = atan left( a_s over a_n right) = 26.579 left[ deg right]
## Water Flowing through Funnel (4.52)
Water flows steadily through a funnel. Throughout most of the funnel the flow is approximately radial (along a rays from O) with a velocity U = c over r^2 , where r is the radial coordinate and c is a constant. If the velocity is U_A = 0.4 left[ m s^{-1} right] at r_A = 0.1 left[ m right] . Determine the acceleration at point A and B.

U = c over r^2 ~ rightarrow ~ c = U_A r_A^2 = 0.4 left[ m s^{-1} right] left(0.1 left[ m right]right)^2 = 0.004 left[ m^3 s^{-1} right]
a_A = U_A { partial U } over { partial s } = - U_A {partial U} over { partial r} = 2 U_A c over { r_A^3 } = 2 times 0.4 left[ m s^{-1} right] { 0.004 left[ m^3 s^{-1} right] } over {left( 0.1 left[ m right] right)^3 } = 3.2 left[ m s^{-2} right]
r_B = sqrt{ left( 0.06 left[ m right] right)^2 + left( 0.1 left[ m right] right)^2 } = 0.1166 left[ m right] , U_B = c over r_B^2 = 0.294 left[ m s^{-2} right]
a_B = 2 U_B c over { r_B^3 } = 2 times 0.294 left[ m s^{-1} right] { 0.004 left[ m^3 s^{-1} right] } over {left( 0.1166 left[ m right] right)^3 } = 1.484 left[ m s^{-2} right]
## Bicycle ride to the beach (4.59)
A bicyclist leaves from her home at 9 A.M. and rides to a beach 40 mi away. Because of a breeze off the ocean, the temperature at the beach remains T_beach = 60 left[ circle{}F right] throughout the day. At the cyclist’s home the temperature increases linearly with time, going from T_{home,9am} = 60 left[ circle{}F right] at 9am. to T_{home,1pm} = 80 left[ circle{}F right] by 1pm. The temperature is assumed to vary linearly as a function of position between the cyclist’s home and the beach. Determine the rate of change of temperature observed by the cyclist for the following conditions:
a) as she pedals 10 mph through a town 10 mi from her home at 10am
b) as she eats lunch at a rest stop 30 mi from her home at noon;
c) as she arrives enthusiastically at the beach at 1 P.M., pedaling 20 mph.

T = T_0 + a x t ~ rightarrow ~ a = 5 over 40 left[ circle{}F mi^{-1} hr^{-1} right]
DT over Dt = { partial T } over {partial t} + u { partial T } over { partial x} ~ rightarrow ~ DT over Dt = ax + u at
x = 30 left[ mi right], t = 1 left[ hr right], u = - 10 left[ mph right] ~ rightarrow ~ DT over Dt = 15 over 4 left[ circle{} F hr^{-1} right] - 5 over 4 left[ circle{} F hr^{-1} right] = 2.5 left[ circle{}F hr^{-1} right]
x = 10 left[ mi right], t = 3 left[ hr right], u = 0 left[ mph right] ~ rightarrow ~ DT over Dt = 5 over 4 left[ circle{} F hr^{-1} right] =1.2 5 left[ circle{}F hr^{-1} right]
x = 0 left[ mi right], t = 0 left[ hr right], u = - 20 left[ mph right] ~ rightarrow ~ DT over Dt = - 10 left[ circle{}F hr^{-1} right]
## Temperature Distribution (4.60)
The temperature distribution in a fluid is given by T = 10 left[ circle{} C m^{-1} right] x + 5 left[ circle{} C m^{-1} right] y , where x and y are the horizontal and vertical coordinates in meters and T is in degrees centigrade. Determine the time rate of change of temperature DT over Dt = { partial T} over { partial t } + vec{U} cdot nabla left( T right) = { partial T } over { partial t } + u { partial T } over { partial x } + v { partial T } over { partial y } of a fluid particle traveling:
a) horizontally with velocity u = 20 left[ m s^{-1} right] and v = 0 left[ m s^{-1} right] or
b) vertically with u = 0 left[ m s^{-1} right] , v = 20 left[ m s^{-1} right] .

DT over Dt = { partial T } over {partial t} + u { partial T } over { partial x} + v { partial T } over { partial y } = 0 + u 10 + v 5 = 400 left[ circle{}C s^{-1} right]
DT over Dt = 0 + 20 left[ m s^{-1} right] 10 left[ circle{} C m^{-1} right] + 0 left[ m s^{-1} right] 5 left[ circle{} C m^{-1} right] = 200 left[ circle{}C s^{-1} right]
DT over Dt = 0 + 0 left[ m s^{-1} right] 10 left[ circle{} C m^{-1} right] + 20 left[ m s^{-1} right] 5 left[ circle{} C m^{-1} right] = 100 left[ circle{}C s^{-1} right]
## Triangular Channel (4.72)
Water flows through the w = 2 left[ m right] wide rectangular channel with a uniform velocity of U = 3 left[ m s^{-1} right] .
a) Directly integrate {dB_out} over dt = int from { cs } { %rho b {vec {U}} cdot {bold{hat{n}}} dA } with b = 1 to determine the mass flowrate dm over dt in left[ kg s^{-1} right] across section CD of the control volume ( %rho = 1000 kg m^{-3} ).
b) Repeat part (a) with b = 1 / %rho where %rho is the density. What is the physical interpretation of part b?

dm over dt = int from { cs } {%rho vec { U } cdot { bold{hat{n}}} dA}
dA = w over {cos %theta} dy , {vec {U}} cdot {bold{hat{n}}} = U cos %theta
dm over dt = int from { y = 0} to {h} {%rho U cos %theta w over {cos %theta} dy} = %rho U w left[ y right]_0^h = %rho U w h = 3000 left[ kg s^{-1} right]
 {dV} over {dt} = int from { y = 0} to {h} {U cos %theta w over {cos %theta} dy} = U w left[ y right]_0^h = %rho U w h = 3 left[ m^3 s^{-1} right]
## Moving Container (4.74)
Water flows from a nozzle with a speed of U = 10 left[ m s^{-1} right] and is collected in a container that moves toward the nozzle with a speed of U_{cv} = 2 left[ m s^{-1} right] . The moving control surface consists of the inner surface of the container. The system consists of the water in the container at time t = 0 left[ s right] and the water between the nozzle and the tank. The jet from the nozzle to the tank has constant diameter stream d = 0.1 left[ m right] . DV_sys over Dt = {partial V_cv} over {partial t} + int from {cs} { {vec {U}} cdot {bold{hat{n}}} dA} = 0
a) At time t_0 = 0 left[ s right] , what volume of the system is outside of the control volume?
b) At time t_1 = 0.1 left[ s right] what volume of the system remains outside of the control volume?
c) How much water enters the control volume during this time period?
d) Repeat the problem for t_2 = 0.3 left[ s right] .

{D b m_{sys}} over {Dt} = {D b m_{cv}} over { partial t} + int from {cs} { %rho b {vec {U}} cdot {bold{hat{n}}} dA} ~ rightarrow ~ DV_sys over Dt = {partial V_cv} over {partial t} + int from {cs} { {vec {U}} cdot {bold{hat{n}}} dA} = 0 ~ rightarrow ~ {partial V_cv} over {partial t} = -{ {vec {U}} cdot {bold{hat{n}}} A}
V_{sys,t_0} - V_{cv,t_0} = {d^2} over 4 %pi l = left( 0.1 left[ m right] right)^2 over 4 %pi 3 left[ m right] = .02355 left[ m^3 right]
V_{sys,t_1} - V_{cv,t_1} = {d^2} over 4 %pi left[ l - left( U + U_cv right) t_1 right] = left( 0.1 left[ m right] right)^2 over 4 %pi 3 left[ m right] = .01413 left[ m^3 right]
{partial V_cv} over {partial t} = -{ {vec {U}} cdot {bold{hat{n}}} A} = d^2 over 4 %pi left( U + U_cv right) ~ rightarrow V_{ cv,t} - V_{ cv,t_0 } = int from {t = t_0 } to {t_1} { {partial V_cv} over {partial t} dt} = {d^2} over 4 %pi left( U + U_cv right) t
V_{ cv,t_1} - V_{ cv,t_0 } = 0.00942 left[ m^3 right]
# Chapter
## Water Flow through Blades (5.4)
Water flows %rho_water = 1.94 left[ slugs over ft^3 right] out through a set of thin, closely spaced blades with a speed of U = 10 left[ fps right] around the entire circumference of the outlet. Determine the mass flowrate through the inlet pipe.

U = 10 left[ fps right] ~ rightarrow ~ U_r = U cos %theta = 5 left[ fps right] ~ "and" ~ U_n = U sin %theta
Q = U_r A = U cos %theta * 2 R %pi h = 5 left[ fps right] 2 times 0.6 left[ ft right] 3.14 times 0.1 left[ ft right] = 1.88 left[ ft^3 over s right]
dot{m} = Q %rho = 3.66 left[ slugs over s right]
## River Confluence (5.20)
Two rivers merge to form a larger river. At a location downstream from the confluence before the two streams completely merge, the nonuniform velocity profile is as shown and the depth is 6 ft. Determine the value of U .

U_1 = 3 left[ fps right] , w_1 = 50 left[ ft right] , h_1 = 3 left[ ft right] , U_2 = 4 left[ fps right] , w_2 = 80 left[ ft right] , h_2 = 5 left[ ft right]
U_3 = 0.8 U , w_3 = 30 left[ ft right] , d_3 = d_4 = 6 left[ ft right] , U_4 = U , w_4 = 70 left[ ft right]
Q_1 = U_1 A_1 = U_1 w_1 h_1 , Q_2 = U_2 w_2 h_2 , Q_3 = U_3 w_3 h_3 , Q_4 = U_4 w_4 h_4

0.8 U w_3 h_3 + U w_4 h_4 = U_1 w_1 h_1 + U_2 w_2 h_2 = 3.63 left[ fps right]
## Water Jet Tipping a Block (5.36)
A 10-mm-diameter jet of water %rho_water = 1000 left[ kg m^{-3} right] is deflected by a homogeneous rectangular block ( d = 15 left[ mm right] , h = 100 left[ mm right] , w = 200 left[ mm right] ) that weighs 6 N. Determine the minimum volume flowrate needed to tip the block.

dot{m} = %rho_water Q , U = Q over A ~ rightarrow ~ {Q} over { R^2 %pi }
dot{m} U h over 2 = W d over 2 ~ rightarrow ~ %rho_water Q^2 over {R^2 %pi} h over 2 = W d over 2 ~ rightarrow ~ Q = sqrt{ { W d R^2 %pi } over { %rho_water h }} = 2.66 times 10^{-4} left[ m^3 s^{-1} right]
## Flow through bend (5.40)
Water flows through a horizontal bend and discharges into the atmosphere. When the pressure gage reads 10 psi. , the resultant x-direction anchoring force, F_Ax , in the horizontal plane required to hold the bend in place is . Determine the flowrate through the bend and the anchoring force, F_Ay in the y-direction, required to hold the bend in place.
Note: {%gamma} = 62.4 lb over ft^3 , %rho = 1.932 slug over ft^3 , .

Continuity: Q_{italic{"in"}} = Q_out = Q ~ rightarrow ~ U_{italic{"in"}} A_{italic{"in"}} = U_out A_out ~ rightarrow ~ U_out = {U_{italic{"in"}} A_{italic{"in"}} over A_out , ~ U_{italic{"in"}} = {U_out A_out} over A_{italic{"in"}}}
Linear momentum in x-direction, left(+ U_{italic{"in"}} right) left(- dot m_{italic{"in"}} right) + left(-U_out cos%theta right) left(+ dot m_out right) = P_1 A_{italic{"in"}} - F_Ax
{Q} over {A_{italic{"in"}}} left(- %rho Q right) + left[ left(Q over {A_{italic{"in"}}} right) left(A_{italic{"in"}} over A_out right)cos%theta right]left( %rho Q right) = P_1 A_{italic{"in"}} - F_Ax ,
Q = sqrt {{F_Ax - P_1 A_{italic{"in"}}} over {%rho_water({1 over A_{italic{"in"}}}+{cos%theta} over {A_out})}} = sqrt {{1440 - 10 times 144 times 0.2} over {1.932 left({1 over 0.2}+{{cos 45} over 0.1} right)}} = 7.04 ft^3 over s
Linear momentum in y-direction: ,
left({Q over A_out} sin%theta right) left(- %rho Q right)= - F_Ay ~ rightarrow ~ F_Ay = %rho_water {Q^2} over {A_out} sin %theta = 1.932 {7.04^2} over {0.1} sin 45 = 674 lb
## Tank Mounted on Cart (5.46)
Water flows steadily from a tank mounted on a cart. After the water jet leaves the nozzle of the tank, it falls and strikes a vane attached to another cart. The cart's wheels are frictionless, and the fluid is inviscid. a) Determine the speed of the water leaving the tank, U_1 , and the water speed leaving the cart, U_2 . b) Determine the tension in rope A . c) determine the tension in rope B .

Bernoulli Equation: z_1 + p_1 over %gamma + U_1^2 over {2g} = z_2 + p_1 over %gamma + U_2^2 over {2g} = z_3 + p_3 over %gamma + U_3^2 over {2g}
z_1 = 4 left[ m right], z_2 = 0 left[ m right], z_3 = 6 left[ m right] , p_1 = p_2 = p_3 = 0 left[ kPa right] , U_3 = 0 left[ m s^{-1} right]
4 left[ m right] + {0 left[ kPa right]} over {%gamma} + {U_1^2} over {2g} = 6 left[ m right] + {0 left[ kPa right]} over {%gamma} + {0 left[m s^{-1} right]}^2 over {2g} ~ rightarrow ~ U_1 = sqrt { 2g left(6 - 4 right) left[m right]} = 6.26 left[ m s^{-1}right]
Linear momentum on tank: left(+ U_1 right) left(dot m_1 right) = F_A ~ rightarrow ~ F_A = U_1 %rho Q_1 = {U_1}^2 %rho A_1 = 391.876 left[ N right]
Linear momentum on vane:
left(+ U_1 right) left(- dot m_1 right) + left(+ U_2 right) left(+ dot m_2 right) = F_B - F_A , and also we have
Q_1 = Q_2 ~ rightarrow ~ dot m_1 = dot m_2 , But U_1 ≠ U_2 , U_1 <> U_2
z_1 + {U_1}^2 over {2g} = {U_2}^2 over {2g} ~ rightarrow ~ U_2 = sqrt{2g z_1 + U_1^2} = sqrt{2 times 9.81 times 4 + 6.26^2} = 10.84 m/s
%rho Q left( U_2 - U_1 right) = F_B - F_A ~ rightarrow ~ %rho U_1 A_1 left( U_2 - U_1 right) = F_B - F_A
F_B = F_A + %rho U_1 A_1 left( U_2 - U_1 right) = 675 left[ N right]
## Leaky tank (5.48)
Water {%rho}_{H_{2}O} = 1000 kg m^{-3} is added to the tank through a vertical pipe to maintain a constant (water) level. The tank is placed on a horizontal plane which has a frictionless surface. Determine the horizontal force, F , required to hold the tank stationary. Neglect all losses.

%rho U_1^2 over 2 = %rho g h_1 ~ rightarrow ~ U_1 = sqrt{ 2 g h_1} , %rho U_2^2 over 2 = %rho g h_2 ~ rightarrow ~ U_2 = sqrt{ 2 g h_2}
F + %rho U_1 A_1 U_1 - %rho U_2 A_2 U_2 = 0 ~ rightarrow ~ F = %rho left( U_2^2 A_2 - U_1^2 A_1 right) = 2g %rho left[ h_2 A_2 - h_1 A_1 right]
F = 2 times 9.81 left[ m s^{-1} right] 1000 left[ kg m^{-3} right] left( 2 left[ m right] 6.25 times 10^{-4} left[ m right] - 1 left[ m right] 1.25 times 10^{-3} left[ m right]right) = 0 left[ N right]
## Suspended hemisphere (5.56)
A vertical jet of water %rho = 1.94 left[ slug over ft^3 right] having a nozzle exit velocity of 15 ft/s with a diameter of 1 in. suspends a hollow hemisphere. If the hemisphere is stationary at an elevation of 12 in., determine its weight.

%rho U_0^2 over 2 = %rho U_1^2 over 2 + %rho g h ~ rightarrow ~ U_1 = sqrt{ U_0^2 - 2 g h} , dot{m} = %rho U_0 %pi d^2 over 4
F_jet = %rho Q U_1 = %rho U_0 %pi d^2 over 4 sqrt { U_0^2 - 2 g h } = 2.0114 left[ lb_f right] , W_hem = 2 F_jet = 4.022 left[ lb_f right]
## Pelton Wheel (5.74)
A Pelton wheel vane directs a horizontal, circular cross-sectional jet of water ( %rho = 1.94 left[ slug over ft^3 right] ) symmetrically. The jet leaves the nozzle with a velocity of 100 left[ fps right] . Determine the x-direction component of anchoring force required to (a) hold the vane stationary, (b) confine the speed of the vane to a value of 10 left[ fps right] to the right. The fluid speed magnitude remains constant along the vane surface.

a) Stationary
U_{ italic{"in"} } = U_out = U ~ rightarrow ~ A_{ italic{"in"} } = A_out = A = {D^2} over 4 %pi , Q = UA = {U {D^2} over 4 %pi} , dot{m} = %rho Q = %rho U D^2 over 4 %pi
U_x = U cos %theta
left( + U right) left( - dot{m} right) + left[ U cos left( %pi - %theta right) right] left( + dot{m} right) = left( + U right) left( - dot{m} right) + left(- U cos %theta right) left( + dot{m} right) = - F_x
F_x = U left( 1 + cos %theta right) dot{m} = %rho U^2 { D^2 } over { 4 } %pi left( 1 + cos %theta right) = 180.63 left[ lb right]
b) Moving
W = U - V ,
## Fighter Jet (5.76)
Thrust vector control is a technique that can be used to greatly improve the maneuverability of military fighter aircraft. It consists of using a set of vanes in the exit of a jet engine to deflect the exhaust gases. (a) Determine the pitching moment (the moment tending to rotate the nose of the aircraft up) about the aircraft’s mass center (cg) for the conditions indicated in the figure. (b) By how much is the thrust (force along the centerline of the aircraft) reduced for the case indicated compared to normal flight when the exhaust is parallel to the centerline?

U_x = U_out cos %theta ,

T = F_z R = 3338.5 left[ lb right] 20 left[ lb right] = 66,769 left[ lb ft right ]
F_{x,%theta} = U_{ italic{"in"} } left( - dot{m} right) + U_{ x } left( + dot{ m } right) = dot{m} left( U_out cos %theta - U_{ italic{"in"}} right) = 18,967 left[ lb right]
F_{x, 0} = U_{ italic{"in"} } left( - dot{m} right) + U_{out} left( + dot{ m } right) = dot{m} left( U_out - U_{ italic{"in"}} right) =19,200 left[ lb right]
F_{ x,0 } - F_{ x, %theta } = 233.33 left[ lb right]
## Spinning Sprinkle (5.88)
Five liters/s of water enter the rotor along the axis of rotation. The cross-sectional area of each of the three nozzle exits normal to the relative velocity is 18 left[ mm^2 right] . How large is the resisting torque required to hold the rotor stationary? How fast will the rotor spin steadily if the resisting torque is reduced to zero and (a) %theta = 0^{ o } , (b) %theta = 30^{ o } , (c) %theta = 60^{ o } .

a)
U_n = U_out = Q over { 3A } , F_n = %rho Q U_n = %rho {Q^2} over {3A} = 462.96 left[ N right]
T = r F_n = %rho {Q^2} over {3A} r = 231.48 left[ N m right]
T = %rho Q W r = 0 ~ rightarrow ~ W = U_n - %omega r ~ rightarrow ~ U_n = {Q} over {3A} = r %omega ~ rightarrow ~ %omega = Q over {3rA} = 185.19 left[ rad s^{-1} right]
b)
U_n = U_out cos %theta = Q over { 3A } cos %theta , F_{n,%theta = 30^{o}} = %rho Q U_n cos %theta = %rho {Q^2} over {3A} %theta = 401 left[ N right]
T_{%theta = 30^{o}} = %rho Q U_n = %rho {Q^2} over {3A} cos %theta r = 200.5 left[ N m right] , T_{%theta = 60^{o}} = 115.74 left[ N right]
W = U_n - %omega r ~ rightarrow ~ U_n = {Q} over {3A} cos %theta = r %omega ~ rightarrow ~ %omega = Q over {3rA} cos %theta
%omega_{%theta = 30^{o}} = 160.38 left[ rad s^{-1} right] , %omega_{%theta = 60^{o}} = 92.6 left[ rad s^{-1} right]