Prof. Dr.
Christian Münker
Analog Filters 2
Implementation and Higher Order
München, 2018

---
Filter Design Flow
Specifications:	Define pass / transition (= don't care) / stop band(s)
„Bandpass“:	Basic ideal filter type
„Chebychev“: Approximation method to the ideal low-pass filter
„2nd order“:	Required filter order
„Sallen-Key“:	Hardware implementation

---
Overview
- Filter types and specs: Ideal and not so ideal
- What's that pole / zero stuff, anyway?
- Second order filter functions and characteristics
- There is no zero tolerance: Rollin' the dice at Monte Carlo
- Second order basic filters: Implementations
- Higher order filter approximations: The good, the bad and the ugly

---
Hardware Filter Implementations and Topologies
What's the „optimum“ filter implementation?
→ Depends on goals & constraints:
- Bandwidth / maximum power consumption?
- Robustness against passive (R / L / C tolerance) and
  active parameter variations (OPAmp gain, bandwidth)
- Digital signal processing further down the line?
- Component availability (tolerance, component values)
- Cost / weight / size
- Available design know-how
- ...

---
Hardware Implementations (just a selection ...)
Passive Analog: RC, RLC, transmission lines - lots of different topologies
Active Analog: Buffered RC, Multiple-Feedback (FB) Infinite-Gain, Sallen-Key, Double-T notch, (Negative) Impedance Converter (NIC), State-Variable, …
Not treated here:
Switched Capacitor: Replace Rs in ICs (large chip area, tolerances up to ± 40%) by switched Cs (small, precise)
Digital: IIR with lots of different topologies derived from analog filters,
various FIR algorithms (DFT based, optimizers based zero placement, ...)
(Nearly) extinct:
Special group delay requirement or analog (bucket brigade) delay filters → FIR
High-order analog filters with precision matching requirements → go digital
If you do need special analog filters, dig up literature from the 50s … 90s (LC, active RC)

---
Passive RC-Filters
Low power consumption (but usually needs amps at input and output)
Always stable
Cascading is difficult; strong interaction between stages, difficult to design
Only damping and real poles and zeros possible → very limited steepness
Useful when fSB >> fPB (RF interferer, Sigma-Delta ADC or DAC)
 u1
 u2
 Z1
 R2
C1
 R1

---
Passive LC-Filters
5th order doubly terminated LC ladder filter
- Much better properties than passive RC-Filters (losses, selectivity, design flow, filter transforms, …)
- But: Inductors are expensive and sensitive to noise coupling
- Very common for RF applications (no alternative due to high frequencies)
- Zillions of topologies
- Also very common as a prototype for active RC-filters:
  - Inductors are replaced by Negative Impedance Converters or
  - System function is „simulated“ by integrator blocks (→ state variable filters)

---
Buffered RC-Filters
OPA / transistor decouples RC-sections → easier design, more flexibility, gain possible
Can be cascaded easily to obtain higher orders, always stable
Easy to design with gain
Still only real poles and zeros possible, limited steepness
R2
 u2
C2
R1
 u1
C1
 u2
 u1
C2
R2
C1
R1
[Speaker Notes: I_r = i_C = U_1/R_1 ; U_c = -U_2 I_c = - CdU2/dt dU2/dt = - U_1 / CR_1 Nutze integrierende Wirkung i,C -> U Übung: Differenzierer?]

---
RC-Filters with negative feedback
alignl {alignc A_U^N`=`u_2 over u_1`=`1`+`Z_2 over Z_1} newline A_U^I`=`u_2 over u_1`=`-Z_2 over Z_1
R1 = 1 kΩ, C1 = 1,59 μF, R2 = 100 kΩ, C2 = 79,6 pF
fP1 = 1 / (2 π R1C1 ) = 100 Hz, fP2 = 1 / (2 π R2C2 ) = 20 kHz, f1 = 1 / (2 π R2C1 )	= 1 Hz
Implement DC-gain without additional components
Not all frequency characteristics can be realized using only Rs and Cs: Try e.g. creating a 2nd order low-pass
Always provide a DC path for both inputs
Still only real poles
What's the transfer function of both circuits above, what's their (dis)advantage?
R1
u1 (t)
u2 (t)
C2
C1
R2
AI: Inv
R1
u1 (t)
u2 (t)
C2
C1
R2
AN: Non-Inv
[Speaker Notes: I_r = i_C = U_1/R_1 ; U_c = -U_2 I_c = - CdU2/dt dU2/dt = - U_1 / CR_1 Nutze integrierende Wirkung i,C -> U Übung: Differenzierer?]

---
Sallen-Key Filter Topology: Lowpass
- We want to obtain complex poles as well
  → only possible with positive feedback !
- The amount of gain K influences stability and filter characteristics
- Also known as Positive Gain Voltage-Controlled Voltage-Source (VCVS) filter
- Gain block is usually realized with an
  OPAmp in non-inverting configuration
www.electronics-tutorials.ws/filter/second-order-filters.html
en.wikipedia.org/wiki/Sallen%E2%80%93Key_topology
http://electronotes.netfirms.com/EN191.pdf
R2
 u2
 K
C1
R1
 u1
C2
bold{alignc K`=`1`+`R_B ` / `R_A}
R2
C1
 u2
C2
R1
 u1
RB
RA
R2
 u2
C2
R1
 u1
C1
R2
 u2
C2
R1
 u1
C1

---
Other Sallen-Key Response Types
Derive Sallen-Key structures from 2nd order passive RC-filters:
Lowpass
Highpass
Not very common, better use Multiple-Feedback Filter (coming soon) for BP
How do we design a band-pass with wide bandwidth yet steep transistions?
Narrow Bandpass
R1
C2
 u2
 K
C1
R2
 u1
R1
C2
 u2
 K
R3
R2
 u1
C3
R2
 u2
 K
C1
R1
 u1
C2

---
a) Equal Component Sallen-Key Low-Pass Filter
- Goal: setting real and imaginary part of a pair of complex poles
- 5 degrees of freedom (= component values) and only 2 design targets:
Option a): Use equal components C1 = C2 = C and R = R1 = R2 , select K for desired filter characteristic:
alignl drarrow ~{alignc H (s)`=` { K over {R_1 R_2 C_1 C_2}} over {s^2 + s left[ {1-K}over{R_2 C_2} + 1 over {R_1 C_1} + 1 over {R_2 C_1} right] + 1 over {R_1 R_2 C_1 C_2}}}
{alignc drarrow ~ H(s)`=`{ K over {R^2 C^2}} over {s^2 + s {{3-K} over {RC}}underbrace {2 %zeta %omega_n} + {1 over {R^2 C^2}}underbrace {%omega_n^2}} } ~~ {alignc drarrow~ bold{%omega_n `=` 1 over {RC} " and " %zeta `=` {3 - K} over 2} ~drarrow~ bold{R `=` 1 over {%omega_n C} " and " K`=` {3 - 2 %zeta} }}
Tip: Select C first (tighly tolerated capacitors are difficult to find)!
R2
C1
 u2
 K
C2
R1
 u1

---
Sallen-Key Gain K and Filter Characteristics
{alignc bold{%omega_n `=` 1 over {RC} " and " %zeta `=` {3 - K} over 2} " or " Q`=`1 over {3-k}}
Plot K and ζ in same diagram:
45°
1/√2
½
ζ=1
¼
0
√3/2
Oscillator
0 dB
-ωn
 jωn
jω
σ
16%
1.25 dB
0 dB
4%
44%
Bessel
Butterworth
0%
Chebychev
6.3 dB
Overshoot
Peaking
(Over)critical
damping
=
passive RC
K = 1
2
2.5
1.586
1.268
3

---
b) Unity Gain Sallen-Key Filter (K = 1) with R = R1 = R2
Option b): Set K = 1 to eliminate tolerance
of gain setting resistors (or use an
emitter follower – cheap & cheerful !)
- Less GBW requirement for OPA
  (but needs more phase margin)
- K = 1 yields ζ = 1 for C1 = C2 and R = R1 = R2 → only real poles !
- Obtain complex poles by choosing C1 ≠ C2 :
alignl `{alignc H (s)`=` { 1 over {R^2 C_1 C_2}} over {s^2 + s left[ 2 over {R C_1} right]underbrace {2 %zeta %omega_n} + {1 over {R^2 C_1 C_2}}underbrace { %omega_n^2}}} " for " R =R_1 =R_2 " and " K = 1
	Special-valued
Cs required!
{alignc drarrow~ %omega_n `=` 1 over {R sqrt{C_1 C_2}} " and " %zeta `=` sqrt{C_1 C_2} over C_1 ~drarrow~ bold{ {C}_1 `=`sqrt{ C_1 C_2} over %zeta `=`{1} over {%zeta R %omega_n}"; "{ C}_2 `=`{%zeta} over {R %omega_n} }}
R
C1
 u2
C2
R
 u1
R
C1
 u2
C2
R
 u1

---
c) Unity Gain Sallen-Key Filter (K = 1) with C = C1 = C2
Option c): Choose K = 1, C = C1 = C2 and R1 ≠ R2 for „straight“ C-values:
alignl `{alignc H (s)`=` { 1 over {R_1 R_2 C^2}} over {s^2 + s {{R_1 + R_2} over {R_1 R_2 C} }underbrace {2 %zeta %omega_n} + {1 over {R_1 R_2 C^2}}underbrace {%omega_n^2}} " for " K = 1 " and " C = C_1 = C_2}
`{alignl {alignc drarrow~ {%omega_n `=` 1 over {C sqrt{R_1 R_2}}} `=`1 over {C overline{R}}}} " and " {alignc {%zeta `=` 1 over {2 %omega_n }{R_1 + R_2} over {R_1 R_2 C}`=`{R_1 + R_2} over {2 sqrt{R_1 R_2}}}`=`{R_1 + R_2} over {2 overline{R}} " with " overline{R} `=` sqrt{R_1 R_2}}
Slightly more difficult
calculation of component values!
{alignc drarrow~ { R_1 `=` 2 %zeta {overline{R}} - R_2 " and " bold {R_2 `=`{overline{R}}^2 over R_1 }} ~drarrow ~bold {R_1 ^2 `=` 2 %zeta {overline{R}}R_1 + {overline{R}}^2 }}

---
Excercise: Sallen-Key Prototype Filters
- Draw the prototype filter for a Sallen-Key low-pass with C = C1 = C2 = 1 F and R = R1 = R2 = 1 Ω and Chebychev characteristic (1.25 dB ripple, K = ?) and
- Tip: Use Components → Opamps → UniversalOpamp2
- Denormalize the filter for ωn = 10 kHz
- Simulate frequency and step response
- Try to explain the loss of attenuation
  at higher frequencies *
- How could you improve this behaviour?
- Redesign for K = 1 and R1 = R2
- Monte Carlo: find the sensitivity against
  GBW / component variations!
* Read TI application report SLOA049b „Active Filter Design“
V1
5
V2
-5
C2
100n
C1
100n
R1
10k
R2
10k
V3
AC 1 0
R3
{(K-1)*10k}
R4
10k
U1
V-
V-
V+
V+
IN
OUT
.ac oct 100 10 10Meg
.param K = 2.0
+
-

---
Multiple-Feedback Infinite-Gain (MFB or MFIG) Filter
built around Differentiator
Bandpass
- „Infinite Gain“ = OpAmp without local gain setting
- Better suited for filters than Sallen-Key when
  - high Q is required (typically for Q > 3, especially narrow BP-filters)
  - gain accuracy (especially unity-gain) in the passband is not important
  - fully-differential filters have to be implemented
- For calculations see e.g. http://electronotes.netfirms.com/EN191.pdf
C
 u2
R1
 u1
R2
C
 u'
 u2
R2
C
 u'

---
State-Space Representation of H(s)
Higher order linear differential / integral equations (→ LTI system H(s) ) can be converted into sets of first order differential / integral equations
An Nth order LTI system can be described as a state-space model with N state variables x(t) resp. X(s), written as vectors
Input signal u(t), output signal y(t) (scalars) and the state variables x are connected via matrix A, vectors B, C and scalar d
Here: single-input, single-output (SISO), but MIMO is possible as well
matrix{bold int x(t)#`=`# bold A bold x(t) # +` # bold B u(t) ## y(t) #`=`# bold C bold x(t) # +` # d u(t)}
matrix{s^-1 bold X(s)#`=`# bold A bold X(s) # +` # bold B U(s) ## Y(s) #`=`# bold C bold X(s) # +` # d U(s)}
H(s) `=` {Y(s)} over {U(s)}
A
B
C
z-1
z-1
s -1
d
Y(s)
U(s)
X
●–○

---
State-Space Representation of System
s-domain:	Rational functions using only integration, gain operations and summations can be realized as an anlog circuit!
alignc Y (s)`=` H(s)U(s) `=` {{ a_0 + a_1 s + `dotsaxis `+ a_N s^N }overbrace{:=N(s)}} over {{b_0 + b_1 s + `dotsaxis`+ b_N s^N }underbrace{:=X(s)}}{U(s)} `=` {N(s)} {{U(s)} over {`D(s)}`}underbrace{:=X(s)} `=`N(s) X(s)
alignl`drarrow~ { U(s)`=` X(s)D(s) `=` b_N s^N X(s) + left({b_0 + b_1 s + `dotsaxis`+ b_{N-1} s^{N-1} `}right) X(s)} newline alignl `drarrow bold {s^N X(s)} `=`{alignc 1 over b_N left[U(s)-left({b_0 + b_1 s + `dotsaxis`+ b_{N-1} s^{N-1}}right) X(s)right]} newline ~~~~~~~~~~~~bold{~=`{alignc 1 over b_N left[U(s)-left({b_0 s^-N + b_1 s^-{(N-1)} + `dotsaxis`+ b_{N-1} s^{-1}}right) color red {s^N X(s)}right]}} " (recursive part)"
alignc bold{ Y (s)`=` N(s)X(s) `=` left({ a_0 s^{-N} + a_1 s^-( N-1) + `dotsaxis `+ a_N}right) color red {s^N { X(s)}} } " (transversal part)"

---
State-Space Filter Synthesis Diagram
The latter form of the system function can be implemented directly as a circuit:
matrix{ v_2(t)# {}=`- {alignc 1 over {R C}} int {{v_1(t)} dt}## alignc V_2(s)#{}=` -{alignc 1 over{s R C}}`V_1(s)}
matrix{v_2(t)#{} =`a int v_1(t) dt## V_2(s)# {}=` a s^{-1} V_1(s) }
≡
In the discrete-time domain, these are called „direct form“ filters!
PS: Why don't we use differentiation and differentiators instead?
U(s)
s -1
s -1
s -1
b0
Y(s)
b1
bN-1
1/bN
a0
a1
aN-1
-
sNX(s)
aN
N
X(s)
s -1
a
int`
a
R
C
 v2
 v1

---
State-Variable Filters*: Exercise
1. Partition the circuit into functional blocks (gain blocks, integrators, adders) and draw a functional diagram (signal flow graph)
2. Guess the order
   of the filter
3. Write down the
   transfer function(s)
4. What is the BP center
   frequency ωn ?
* German: „Zustandsvariablen-
oder Universalfilter“
see also http://en.wikipedia.org/wiki/State_variable_filter

---
State-Variable Filters: Solution
{drarrow ~Y_HP(s)} `=` {U_{I N}(s)} `-`{Y_TP(s)} left(alignc k over{s R C} `+` 1 over{(s R C)^2}right) `=`{U_{I N}(s)}left(alignc {(s R C)^2 + s k R C + 1}over {(s R C)^2} right)^{-1}
drarrow {alignc ` H_HP(s) `=` {Y_HP(s)} over {U_{I N}(s)} `=` {(s R C)^2}over{(s R C)^2 + s k R C + 1}`=` {s^2}over{s^2 + s k %omega_n + %omega_n^2} " with " %omega_n = 1 over {R C}} " and " %zeta = k over 2
drarrow {alignc~ H_TP(s)`=` {H_HP(s)} over {(s R C)^2}`=` {%omega_n^2}over{s^2 + s k %omega_n + %omega_n^2} " and "H_BP(s)`=` {H_HP(s)} over {s R C}`=` {s %omega_n}over{s^2 + s k %omega_n + %omega_n^2}}
int` -{alignc 1 over{R C}} int` -{alignc 1 over{R C}}
k
-
-
TP
BP
HP
IN
{alignc 1 over{s R C}} {alignc 1 over{s R C}}
k
-
-
TP
BP
HP
IN

---
State-Variable Filters: Simulation & Sensitivity Analysis
- Verify your results with LTSpice or the breadboard
- Run a Monte-Carlo analysis in LTSpice and vary
  - the GBW – product of the amplifiers and the open loop gain @ DC by ±50%
  - the resistor values by ±50%

---
Pros and Cons of State-Space Filters
- robust against component tolerances, also for high-Q filters (recommended for Q > 10)
- multiple filter characteristics (LP, HP, BP) at the same time
- corner / center frequency and zeta can be tuned independently
high number of OPA's (cost, power, noise)

---
Higher Order Filters
- It's easy to derive H(ω) from H(s) using s = jω
- How do we go the other way? How do we obtain H(ω) and H(s) from the filter specifications (= tolerance bands)?
- Need additional constraints: Order, monotonicity / allowable ripple in PB / SB, group delay variation, overshoot in step response …
- Depending on these constraints, different „optimum“ filter approximations to the ideal characteristics are found
Excellent explanation of approximation functions and the maths behind: www.matheonics.com/tutorial.html !

---
Second-Order System / Biquads
- Higher order system are usually built by cascading 2nd order systems for stability / sensitivity reasons
- Transfer functions with a second order numerator and denominator are called biquadratic („biquad“)
- The numerator has a damping effect („zeros“), the denominator can cause resonant behavior or even instability
- We only regard „all-pole“ filters here with no zeros except at 0 or ∞; additional zeros in the stopband improve attenuation
- Zeros are implemented using notches - at the cost of higher complexity
A_U (s)`=` {U_2(s)} over {U_1 (s)} `=`{ a_0 + a_1 s + a_2 s^2 } over {b_0 +b_1 s + b_2 s^2}

---
A slope like this is BUTTER worth
Optimization target Butterworth: Monotonous magnitude transfer function with maximum flatness in the passband
- Squared magnitude function of N-th order Butterworth filter:
- First 2N -1 derivatives are zero at ω = 0 → maximum flatness!
- Maximum gain at DC with H(jω = 0) = 1
- Cutoff-frequency (-3dB) at ωC = ωn (regardless of order N)
- Roots of H(s) are distributed along a semi-circle with radius ωn :
alignc bold{left lline H_{LP,But}("j" %omega) right rline^2 `=`{ 1 } over {1 `+` left({%omega}over{%omega_n}right)^{2 N}}}
alignc left lline H("j" %omega) right rline^2_{%omega = s/"j" } `=`H(s)H(-s) `=`{ 1 } over {1 `+` left({s}/{"j" %omega_n}right)^{2 N}}"; solve for "1 `+` left({s}/{"j" %omega_n}right)^{2 N}` {`=`} csup"!" 0

---
Overview Butterworth Filter
Butterworth poles are distributed along a circle with radius ωn

---
Butterworth Order
alignc N = left lceil {log left({10^{0.1 A_PB}-1}over {10^{0.1 A_SB}-1} right )} over {2 log %omega_{PB}/%omega_{SB}} right rceil
- Minimum order:
- There are only two parameters – N and ωn – so, usually either PB or SB specifications can be met tightly, the other will be „overengineered“
In comparison to other filter types, the Butterworth filter has a
  - Maximally flat amplitude response
  - Medium frequency selectivity
  - Medium group delay variation / little step overshoot
It is a good compromise for many applications.

---
A shabby (CHEBY) compromise ...
Optimization target Chebychev: Minimum order for a specified passband ripple δPB , spread across the whole passband
- The approximation utilizes Chebychev polynomes of first kind. Their magnitude is bounded by 1 over a given interval x (= PB), touching ± 1 :
- Important tool for approximation
  theory / polynomial interpolation:
  Minimizes the maximum
  error (Minimax approximation)
- cheapest method that just
  fulfills the specs ...
T_0(x) ~~=` 1 newline T_1(x) ~~=` x newline T_2(x) ~~=`2 x^2 - 1 newline T_{n+1}(x) `=` 2 x T_n(x) - T_{n-1}(x)

---
Chebychev Filter
- Squared magnitude function of an N-th order Chebychev filter:
- ε is a parameter depending on the allowable ripple in dB:
- ωPB = ωn (regardless of order N), defining the edge of the passband
In comparison to other filter types, the Chebychev filter has a
  - High frequency selectivity
  - Ripple in the passband (non-monontonous)
  - High group delay variation / strong step overshoot
It is a good choice when high frequency selectivity with a low order is needed and the group delay variation is not so important.
alignc bold{left lline H_{LP,ch}("j" %omega) right rline^2 `=`{ 1 } over {1 `+` %epsilon^2 T_N^2 left({%omega}over{%omega_n}right)}}
alignc bold { %epsilon `=`sqrt {10^{0.1 A_PB`-`1} }}

---
Overview Chebychev Filter
Scale real parts of Butterworth poles with α < 1 (related to ε) → Chebychev!

---
There is nuthing BESSEL vor se phase!
Optimization target Bessel (Thomson) filter: Constant group delay in the passband / no overshoot of step response
Constant group delay = all frequency components have same delay = no overshoot
In comparison to other filter types, the Bessel filter has a
  - Monotonous amplitude response with some droop
  - Low frequency selectivity
  - Lowest group delay variation / no step overshoot
It is best suited when a well defined time domain behaviour is needed.

---
Overview Bessel Filter

---
Comparison of Different 4th Order Filters
Bessel filter
very low selectivity
IH(f)I: monotonous
φ(f): very small non-linearity
Butterworth-Filter
low selectivity
IH(f)I: maximally flat (PB)
φ(f): small non-linearity
Chebyshev filter
medium selectivity
IH(f)I: Ripple in PB (Type 1) or
    SB (Type 2, inverse Cheb.)
φ(f): medium non-linearity
Elliptic filter
maximum selectivity
IH(f)I: ripple in PB and SB
φ(f): large non-linearity
Spezifications
 APB = 1dB, fPB = 1 kHz, ASB = 30 dB, fSB = 2 kHz
ASB=3 dB

---
Implementation of Higher Order Filters
- Always partition transfer function in second-order sections (SOS)
- Coefficients for individual sections can be found in tables (filter prototypes) or by using Python / Matlab (→ tf2sos)
- Individual sections are implemented e.g. as Sallen-Key filters
- Sensitivity analysis is important for higher order, high-Q filters!

---
Exercise: Design a Sixth-Order Butterworth Filter!
- Design a sixth-order Butterworth low-pass filter with ωn = 5 kHz from 3 second-order sections with the Q-factors given below
- The poles of a Butterworth filter all have a radius of ωn – no frequency scaling (FSF = 1) required!
TI: „Active Low-Pass Filter Design“, http://www.ti.com/lit/an/sloa049b/sloa049b.pdf

---
Analog Prototypes in Python
Calculate normalized / denormalized polynome coefficients bb, aa:
import numpy as np
import scipy.signal as sig
[bb,aa] = sig.bessel(L, W_c, analog=True)
[bb,aa] = sig.butter(L, W_c, analog=True)
[bb,aa] = sig.cheby1(L, A_PB_log, W_PB, analog=True)
[bb,aa] = sig.cheby2(L, A_SB_log, W_SB, analog=True)
[bb,aa] = sig.ellip(L, A_PB_log, A_SB_log, W_PB, analog=True)
N = np.poly(bb) # numerator polynome
D = np.poly(aa) # denominator polynome

---
Literature
- Don Lancaster, „Active Filter Cookbok“ (also available in German) – a classic!
- Good introduction: www.electronics-tutorials.ws/category/filter
- TI Application Report SLOA024B „Analysis of the Sallen-Key Architecture“, Texas Instruments, 2002.
- State variable filters: MIT OpenCourseWare, 2.161 Signal Processing: Continuous and Discrete, „Op-Amp Implementation of Analog Filters“, 2008.
- Detailed calculations: electronotes.netfirms.com/EN19x.pdf → EN191, 192, 193, 194
- Active filter overview: sound.westhost.com/articles/active-filters.htm
- U.C. Berkeley, EE247, Integrated Analog-Digital Interface Integrated Circuits, www-inst.eecs.berkeley.edu/~ee247/fa10/lectures.html
- users.ece.gatech.edu/phasler/Courses/ECE6414/Unit1/
  - Lecture #1 : Basics & second order filter implementations
  - Lecture #2 : Higher order filter functions and implementations
- Matheonics, Tutorial 'How to design analog filters', on filter prototypes, approximation functions etc: www.matheonics.com/tutorial.html
- Interactive filter design: www.analog.com/designtools/en/filterwizard/

---
Backup-Slides
Thank you for
your attention !

---
Active Inductors / Negative Impedance Converter
Use a negative impedance converter to convert a capacitor to a ground-referenced inductivity:
© http://sound.westhost.com/articles/active-filters.htm

---
Low-Pass + Notch = Cauer (elliptic) filter
© http://sound.westhost.com/articles/active-filters.htm