# Installation Instructions
## Power Input
### Input Power Requirements
The MicroStar Series Rectifier is designed for operation from 110VAC or 220VAC 1-phase, 50-60 Hz, primary power.. Check the label on the rear of the unit for proper input power requirements
The output capacity of each rectifier is specified on the equipment serial tag located on the back of the unit.
### Input Power Connection
Connect the power cord to the correct supply in accordance with U.L. and/or OSHA specifications or local requirements. Make sure the connections are made with power OFF and under no load.
## Mounting and Cooling Clearance Requirements
The MicroStar Series Rectifier is designed for shelf or 19" rack mounting. Rack mounting requires optional mounting flanges.
Cooling is front to rear. Do not block airflow at the front of the unit and leave 4 inches (10cm) minimum at the rear.
## Output Power Connections
Located at the rear of the DP(R) MicroStar series are two 3/8" bolts or two connectors which are used to connect to the bath. Make sure the connections are tight to reduce heating.

Figure 1.1: Rear Panel
## Remote MicroStar Connection (Optional)
Connect the Remote MicroStar to the power supply with the supplied RJ45 cat5 patch cable supplied. The connection at the Remote MicroStar is on the bottom or rear of the enclosure. The connection to power supply main unit is on the rear of the unit.

Figure 1.2: MicroStar Remote Cat5 Cable

Figure 1.3: Remote MicroStar Panel: Front & Rear Views

## Host Port Connections
The MicroStar Series rectifier can be controlled and monitored by a host (computer, PLC, etc). The host port can be used to monitor and/or control the MicroStar power supply using the ASCII Host Protocol (See section Error: Reference source not found Error: Reference source not found and Appendix Error: Reference source not found Error: Reference source not found for more information).
### RS485 Host Port Connections
The serial host port supports a half duplex RS485 interface. Multiple MicroStar power supplies can be connected to a single RS485 bus (multi-drop). Each device on the RS485 bus is individually addressed using the ASCII Host Protocol. If an RS232 device (such as a PC) will be connected to the MicroStar host port then an RS232 to RS485 converter module is required (not included). See section Error: Reference source not found Error: Reference source not found for host port operation and more information.
Make sure the connections to the host match the signals shown below.
Connecting multiple MicroStar power supplies to a single RS485 network will require Y cables – 2 Male to 1 Female DB9 (Dynatronix#020-0005-07) in order to “daisy chain” the RS485 Host Ports. These Y cables can also be purchased at PCCABLES.COM, Part No.00828, or any similar (9 pin D, 1 F x 2 M) strait-through Y cable can be used. The cables between each unit can be a standard strait-through serial cable.
Figure 1.4: RS485 Wiring Connections

1
5
9
6
RS485 Connections
1 nc
2 nc
3 nc
4 Data B (normal low, goes high)
5 nc
6 nc
7 nc
8 Common
9 Data A (normal high, goes low)
DB9 Female Connector on Back of Unit

Figure 1.5: RS485 Host Connections with 3 Units

Host,
Comp. or PLC
Unit 1

Unit 2

Unit 3

Strait Cable
Y Cable

Y Cable
Strait Cable
Strait Cable
### USB Host/Service Port Connections
The Host/Service USB port can be used as a single connection, short run, Host port. It is also used for downloading firmware upgrades. The USB connection uses a Type B connector. See Appendix Error: Reference source not found Error: Reference source not found for more information on using the USB port.
## Digital I/O Connections
Figure 1.6 shows the Digital Input/Output connector with labels showing the signals on each terminal. When attaching wires to the connector use a 2.5mm (0.1”) flat blade screwdriver inserted into the square opening (blade horizontal) to release the wire clamp. Insert the wire into the round hole next to the screwdriver. Remove the screwdriver to clamp the wire in place.

Figure 1.6: Digital I/O Connector
Bottom of Connector
Wire Clamp Release, Insert Small Flat (2.5mm) Screwdriver
Insert Wire in Round Holes

1
3
5
7
9
11
13
15
2
4
6
8
10
12
14
16
Interlock Enable Input
Alarm Sense Output +
Operate Input
Operate Sense Output -
Gnd
Spare Input +
Gnd
Spare Input -

Operate Sense Output +
Spare Output +
+5V
N.C.
Alarm Sense Output -
Spare Output -
+5V
N.C.

### Digital Inputs
The two standard digital inputs are the Interlock Enable input and the Operate input.
#### Interlock Enable
The Interlock Enable input (Pin 1) when tied to Gnd (Pin 9) allows for proper operation of the supply. When this connection is open supply operation is disabled. If the supply is operating when this input is opened the unit will go into standby and a message will be displayed.
#### Operate Input
The Operate input (Pin 2) when tied to Gnd (Pin 10) activates the output of the supply (Remote Operate/Standby). NOTE: This input must be used to control the output when using the SYS, Error: Reference source not found>Error: Reference source not found, 3>Error: Reference source not found menu item. It is optional in all other modes.
SEE: Section Error: Reference source not found Error: Reference source not found, Error: Reference source not found>Error: Reference source not found, 4>Error: Reference source not found for more information on the options for using this input.

When any one of these digital inputs are closed, the current flowing through the corresponding circuit will be less than 15mA.

External, customer supplied SW1 & SW2 switches, PLC output or similar.
Figure 1.7: Digital Input Connections

1
3
5
7
9
11
13
15
2
4
6
8
10
12
14
16
Interlock Enable Input
Operate Input
Gnd
Gnd
+5V
+5V

Close To Enable
SW1

Close To Operate
SW2
### Digital Outputs
The two standard digital outputs are the Operate Sense and the Alarm Sense.
#### Operate Sense
The Operate Sense (Pins 3 & 4) when configured as shown below can be used to sense whether the unit is in the Operate or Standby condition. The Operate condition will cause current flow thru the circuit and the external opto-coupler shown will be in the “on” state.
#### Alarm Sense
The Alarm Sense (Pins 5 & 6) when configured as shown in Figure 1.8 below can be used to sense if an alarm condition has occurred. An alarm condition will cause current to flow thru the circuit and the external opto-coupler shown will be in the “on” state.

A different voltage source can be applied to the Alarm Sense + (Pin 5) and Operate Sense + (Pin 3) output pins. If the voltage is greater than 5 volts it must have an external current limit resistor to limit the current to 15mA. The maximum voltage allowed on the + input or - output pins is 24V DC.
The maximum current flow through either of the digital outputs is 15mA.

Figure 1.8: Digital Output Connections

1
3
5
7
9
11
13
15
2
4
6
8
10
12
14
16
Gnd
+5V

SW1
Operate Indicator or Input

Alarm Sense Output +
Operate Sense Output +

Alarm Indicator or Input
Operate Sense Output -
Alarm Sense Output -
External, customer supplied LED, Optocoupler sense circuit, PLC input or similar.

## Relay Connections (pump control) – (Option)
The optional relay output can be used to control a chemical pump. It can also be set up as an output that is on while the unit is in operate or to be on when there is an alarm condition. See Section Error: Reference source not found Error: Reference source not found, Error: Reference source not found>Error: Reference source not found, 5>Error: Reference source not found and Error: Reference source not found Error: Reference source not found relay items for more details.
The relay connections are the 3 position terminal strip at the rear of the control enclosure. Figure 1.9 shows the connection points for the relay to control an external device. Relay contacts, common to normally closed, open when the condition controlling the relay is active. Relay contacts, common to normally open, close when the condition is active.
The ratings for the relay contacts are 12 Amps at 125 Volts AC/DC. The terminals accept 24 to 12 gauge wire.

Figure 1.9: Relay Output Connector

Common
Internal Relay

Normally Open

Normally Closed

Removable Terminal Strip

## Analog I/O Connections (Option)
Rectifiers which have the optional analog control will be equipped with the 138-0362-xx card and require customer supplied wiring. Depending on the analog board purchased it will be controlled by either a 4-20mA, 0-5V or 0-10V signal. See Figure 1.10 and Figure 1.11 below for connection diagrams.
See section Error: Reference source not found Error: Reference source not found for analog operation.
The following gives a description of the control and readback signals on the 20 pin socket block.
VOLTAGE CONTROL (VC)
Control of the power supply output voltage can be achieved by connecting the appropriate signal to: Forward Voltage - pins 16 (+) and 15 (-), Reverse Voltage (if reversing unit) - pins 18 (+) and 17 (-).
CURRENT CONTROL (CC)
Control of the power supply output current can be achieved by connecting the appropriate signal to: Forward Current - pins 12 (+) and 11 (-), Reverse Current (if reversing unit) - pins 14 (+) and 13 (-).
VOLTAGE READBACK (VRB)
Monitoring of the power supply output voltage can be achieved by connecting the appropriate sensing circuitry to: Forward Voltage - pins 6 (+) and 5 (-), Reverse Voltage (if reversing unit) - pins 8 (+) and 7 (-).
CURRENT READBACK (CRB)
Monitoring of the power supply output current can be achieved by connecting the appropriate sensing circuitry to: Forward Current - pins 2 (+) and 1 (-), Reverse Current (if reversing unit) - pins 4 (+) and 3 (-).
Pins 9 and 10 can be used for a DC COMMON connection.
Pin 19 and 20 can be used as a connection point for the cabling shields.
NOTE: To reduce the possibility of electrical noise interfering with the proper operation of the control system, use shielded twisted pair for all wiring between the analog controller and the power supply. Belden™ 8761 or equivalent cable type is recommended.
NOTE: The DC COM (pin 9 & 10) are used to connect the power supply’s DC common to the controller's DC common. The shielding for the voltage & current control lines should be earth grounded at the controller and should be cut-off at the power supply. The shielding for the voltage & current readback lines should be earth grounded at the power supply (pin 19 & 20 - SHIELD) and cut-off at the controller. See diagrams below.
NOTE: When using 4-20mA control, the controller’s input channels must be isolated from each other. It is recommended that isolated receivers (ex. OPTO 22 AD3T or equivalent) be used with the curr rb out and volt rb out transmitter channels. These transmitter channels are self powered.
The receiver inputs and transmitter outputs are ground isolated from the power supply’s DC common and are isolated from earth ground as well. However, be aware that both input channels and both output channels of the AI board, do share a common signal ground. In other words, there is no isolation from channel to channel or receiver inputs to transmitter outputs except that provided by the differential inputs. A common ground signal from the Remote Analog Controller is required.
NOTE: Maximum loop resistance that can be in series between the (+) and (-) of the current or voltage readback signals is 400 Ohms
Units that require both Fwd & Rev Current Control and Readback and Fwd & Rev Voltage Control and Readback should be wired as shown in Figure 1.10 below: (If current control is set as the regulation mode, then the voltage inputs are not required. If voltage control is set as the regulation mode, then the current inputs are not required. See NOTE and Figure 1.11 below).
The Current and Voltage readback signals can be monitored at any time no mater what the regulation mode or control source is set to.

NOTE: The analog control card has control of the output current and voltage if it is enabled. To enable analog control it must be in one of the analog control modes. See section Error: Reference source not found Error: Reference source not found, Error: Reference source not found>Error: Reference source not found for more information on the modes.

NOTE: When the 'Analog Control mode' is enabled the unit can only go to operate using the external operate input as described in section 1.6.1.2 Operate Input. The other analog control modes can be put into operate either with the control panel or the host port.

Figure 1.10: Typical Analog Control Wiring (All Signals; Fwd & Rev Current and Fwd & Rev Voltage, Control and Reading)

1
3
5
7
9
11
13
15
17
19
2
4
6
8
10
12
14
16
18
20
- FWD I OUT
- REV I OUT
FWD I OUT +
REV I OUT +
- FWD I IN
- REV I IN
FWD I IN +
REV I IN +
Bottom of Connector

Wire Clamp Release, Insert Small Flat (2.5mm) Screwdriver
Insert Wire in Round Holes and remove screwdriver

- FWD V OUT
- REV V OUT
- FWD V IN
- REV V IN
FWD V OUT +
REV V OUT +
FWD V IN +
REV V IN +

GND
SHIELD
GND
SHIELD

IN
OUT
Analog Controller

IN
OUT

IN
OUT

IN
OUT
Fwd Curr
Fwd Volt
Rev Curr
Rev Volt

Earth
Ground

Shields

Shields

Cable(s)

Signal
Common

NOTE: If any of the analog channels are not being used they need to be jumpered as follows. Figure 1.11 shows how to install jumpers if only the Forward Current channel is being used. This is required for proper operation of settings and readings.
Fwd Current channel is not used, jumper 1 to 11 and 2 to 12.
Rev Current channel is not used, jumper 3 to 13 and 4 to 14.
Fwd Voltage channel is not used, jumper 5 to 15 and 6 to 16.
Rev Voltage channel is not used, jumper 7 to 17 and 8 to 18.

Figure 1.11: Analog Connections - Fwd Current Only (with required jumpers in other channels)
Jumpers
Jumpers

Earth
Ground

Signal
Common

1
3
5
7
9
11
13
15
17
19
2
4
6
8
10
12
14
16
18
20
- FWD I OUT
- REV I OUT
FWD I OUT +
REV I OUT +
- FWD I IN
- REV I IN
FWD I IN +
REV I IN +
Bottom of Connector

Wire Clamp Release: Insert Small Flat (2.5mm) Screwdriver
Insert Wire in Round Hole and remove screwdriver

- FWD V OUT
- REV V OUT
- FWD V IN
- REV V IN
FWD V OUT +
REV V OUT +
FWD V IN +
REV V IN +

GND
SHIELD
GND
SHIELD

IN
OUT
Analog Controller

IN
OUT

IN
OUT

IN
OUT
Fwd Curr

Shield

Shield

Cable(s)

## Master-Slave Connections – (Option)
The Master Slave option allows multiple power supplies to work in unison. There is one unit that is the Master and 1 to 9 Slave units that are slaved to the Master. The slaves use the same timing signals and cycle control durations as the master. Other settings, like current and voltage levels, can be different on the slave versus the master. See section Error: Reference source not found Error: Reference source not found and section Error: Reference source not found Error: Reference source not found for more information.
### Master-Slave Installation
The units will come set up as one Master and one or more Slaves. The serial number of the unit typically determines the order of the master and slave units. The lowest serial number is the master and the following serial numbers are slave1, slave2, etc. If there is just 1 slave, then the master and slave are connected together with one cable that has 15 pin male D Sub connectors on each end. If there is more than 1 slave then there is a special Y cable that goes from the master to the first slave and then possibly more Y cable(s) that go to the other slaves, and finally a normal cable that connects from the last Y cable to the last slave unit. Two connection diagrams are shown below.
Figure 1.12: Connection Diagrams for Single and Multiple Slave Units

Master
Slave

Master
Slave 1

Slave 2

Slave 3

Strait Cable
Strait Cable
Y Cable
Y Cable
Master-Slave Connections with 2 Units
Master-Slave Connections with 4 Units