Investigation of the Hall Effect in Semiconductors
PHYS2170 Lab Report

Abstract:
Introduction:

Semiconductors are often doped to improve its conductivity. There are two types of doping: p-type and n-type. P-type doping a semiconductor will leave that semiconductor with its dominant charge carrier being holes, whereas n-type semiconductors have electrons as the dominant charge carriers. The conductivity (σ) of a sample is related to the number density (n) of the charge carriers by the following equation:
%sigma = n q %mu "where q is carrier charge and " %mu " is the charge mobility." (1)

It is also known that a force is exerted on a moving charged particle according to:
F=q widevec {v_d} times widevec{B} newline "where " widevec {v_d} " is drift velocity and " widevec {B} " is magnetic field strength." (2)

If, for example, the positive charge carriers (holes) are dominant, the resulting force would be upwards if conventional current flows from left to right and the magnetic field goes into the page. Eventually, enough positive charge will accumulate at the top of the doped semiconductor to provide an electric field force that balances this magnetic force. This is represented by the equation:
q widevec {v_d} times widevec{B} + q widevec{E} = 0 newline "where " widevec{E} " is the electric field strength." (3)
As current and electric field strength can be expressed as (respectively), and assuming the current travels along the x-axis:
I = p q lline v_d rline w t newline alignc {"where w is width of sample, t is thickness and p is the positive charge carrier density."} newline V_H = w E newline alignc {"where " V_H " is the Hall voltage."} (4&5)

Using equations 3, 4 and 5:
V_H = {BI} over {p q t} = {BI R_H} over t (6)
Where, for p-type semiconductors:
R_H = 1 over {pq} (7)
And for n-type semiconductors (where, in the equation, 'n' is electron density):
R_H = -1 over {nq} (8)
To calculate the mobility, starting with:
v_d = %mu E_x newline "where " E_x " is the electric field creating the current." (9)
And noting that:
J_x = %sigma E_x = v_d over R_H newline "where " J_x " is the current density." (10)
Results in the simple equation:
%mu = %sigma R_H (11)
Note that in this experiment resistivity is known (and thus its reciprocal – conductivity).

V_H = 1 over 2 (V_H1 - V_H2 ) There is one error that is corrected for in this experiment, and that is a voltage offset, created from misalignment of the measuring probes. Noting that the polarity of the corrected voltage does not change for a reversal in the magnetic field strength, but does for a reversal in current, the voltage can be corrected by using the formula:
(12)

Procedure:

Figure 1: Experimental setup.
The experiment was set up according to figure 1 and calibrated. To calibrate the electromagnet, a Gaussmeter probe was put in the approximate centre of the magnetic field (in the centre with regards to x, y and z directions as labelled in figure 1). Care was taken to ensure that the electromagnetic material was not influenced by an electric field before calibration (so as to ensure that the material had not undergone any magnetic alignment).

Measurements were taken in increments of 0.25 Amps, with the electromagnet poles in its initial position and switched, for both samples. In an effort to demagnetise the electromagnet material, after the poles were switched and before readings were taken, the current through the electromagnet was increased to approximately 1 Amp before being reduced to zero. This was done to ensure the alignment had reached 'saturation' so as to ensure a firm basis point from which to make measurements.

Results:

The Hall voltage for both of the samples can be seen in figure 2. By observing figure 2, it is immediately clear that sample #3369 and #3375 have opposite polarities. The line-of-best-fit for sample #3375 has a slope of 204.468 mV T-1 with a R2 value of 0.99952 and sample #3369 has slope of -194.982 mV T-1 with a R2 value of 0.997613.

Figure 2: Corrected Hall voltage as a function of magnetic field strength, for both samples #3369 and #3375.
This results in values of

Discussion:
Conclusion: