PROJECT WORK SPECIFICATIONS
for renovation of 11265 Otsego Street North Hollywood, CA 91601
Table of Contents

# SUMMARY
This document specifies the work to be done as part of the contract entitled Renovation of the Vartan Piroumian duplex located at 11265 Otsego Street, North Hollywood, CA 91601-3728. This document is incorporated into the aforementioned contract and comprises the complete specification of scope and detail of work to be performed in fulfillment of the aforementioned contract.
# DEFINITIONS
Apartment 1 is the left side apartment when viewing the building from the street.
Apartment 2 is the right side apartment when viewing the building from the street.
Medium grade material shall be interpreted to mean material whose cost has a median value in the range of lowest to highest for that type of product.
# QUALITY OF MATERIAL
Medium grade material. In general, unless approved by owner prior to purchase of material, the quality of all material, products, fixtures and so forth shall be at least medium grade unless the use of a particular model, product line, or grade or level of material is explicitly specified. Unless otherwise noted, all copper piping shall be at least L-type.
Allowances. See Allowances section in contract for information on allowances for materials, fixtures, accessories, etc.
# PRE-CONSTRUCTION CONDITIONS
Existing HVAC systems. The following specifications for the HVAC system describe work that was done as part of the work of a previous contract. The description is listed here for reference only. This work does not need to be redone. HVAC package units have been installed on a metal platform on the building roof. The attic has been reinforced.
80% AFUE, 70K BTUH, gas forced air furnace.
14 SEER 3 ton A/C condensers.
High efficiency 3-ton evaporator coils.
Programmable digital thermostats installed upstairs.
Design new duct system per ACCA manual D design guidelines.
Cut one new return air opening located in hallway at stairway landing.
Cut new air supply opening in bedrooms and upstairs bathrooms.
Run duct through small bedroom closet to first level to supply living rooms and kitchens.
R-6.0 high efficiency metalized silver jacket flexible duct system with vapor barrier.
Install manual controlled volume dampers in all accessible final branches.
Install new bar type register grills.
Seal all metal to metal joints with duct mastic.
Disconnect and cap ducts from old system.
Insulate all exposed sheet metal with 1.5” fiberglass insulation. Secure all new ducting with 1 1/2” galvanized hanger straps per code.
Install all required pads and platforms and heavy gage metal straps to support new equipment.
Install gas lines with stainless steel gas flex connectors with shut off valves for the furnaces.
Run low voltage electrical lines.
Install 110V electrical lines for the furnaces.
Install 220V electrical lines for the condensers.
Install new properly sized refrigeration lines.
Install new ¾ PVC condensation drain lines with automatic flood controlled switches.
Use drop clothes to protect floors and furniture.
Start-up systems and cycle to verify proper operation according to manufactures specifications.
Pressure test lines and ducting.
Pre-construction preparation. Before beginning work, install an air filter for the HVAC air return vent, and seal the vent with rosin paper and tape, to prevent dust, dirt, paint, etc. particles from sanding, spraying and general construction work from damaging the HVAC unit.
Cover bath tubs with two layers of rosin paper to avoid any scratches, nicks, abrasions and general damage to tubs.
Similarly protect sinks, toilets, cabinets and generally all fixtures, furniture, etc. to prevent damage.
# PROJECT PLAN
The work for this job shall be divided into “phases”, listed below in the order in which they shall be performed. The work comprising each phase shall be completed before the work comprising the next phase begins. Generally work shall proceed from back-to-front and inside-to-outside.
Work on apartment 1 (and back structure concurrently if preferable to contractor). Complete apartment 1 (excluding exterior) and back structure so they are in turnkey condition. Owner then vacates apartment 2 and moves into apartment 1.
1. Complete apartment 2 so it is in turnkey condition.
2. Complete main building exterior (front structure), working front-to-back.
Note that the specifications of work below do not necessarily appear in the order in which the work will be done.
# APARTMENT 1 INTERIOR
HVAC SYSTEM. Do the following work on the HVAC system.
HVAC system maintenance. Test HVAC system and verify that is is functioning properly, and, if not, bring it to proper functioning condition. Pressure test lines and ducting. Perform two-year (2-year) scheduled maintenance.
HVAC air return air filter. Contractor shall install SpaceGuard air filter or brand and model filter of equivalent quality. The filter installed should be the kind that lasts for six (6) months.
Programmable thermostat. Install a programmable thermostat in the position specified by owner. Run appropriate wiring from the actual HVAC unit to the thermostat to provide power to the thermostat (low-voltage 24V electrical supply) if such wiring is not already in place. Run the line in the wall, directly down from the attic in line with the thermostat's location. Owner purchases thermostat.
KITCHEN, APARTMENT 1. Do the following work.
Recessed lights. Replace the two (2) six-inch (6”) recessed lighting cans and trim with $58 elegant looking trim. Replace cans if they do not meet code. If so, replace trim only. Consult with owner regarding final solution and material selection.
Kitchen sink pendant light fixture. Install pendant light fixture above kitchen sink. Customer purchases.
Dining room nook chandelier. Move existing chandelier fixture wiring plate about 8” - 12” from its present position. Install new chandelier above nooks. Consult owner for precise location of new wiring plate. Customer purchases.
Electrical wall plates and sockets. Upgrade all existing electrical wall plates and sockets to new equipment.
GFCI wall plates and circuits. Install GFCI wall plates and circuits where necessary to comply with building code.
Dedicated electrical circuits. Wire dedicated circuits for microwave, dishwasher, and any other appliances as required by code.
GFCI wall plates, sockets and circuits. Install GFCI-compliant wall plates and circuits where necessary to comply with building code. Retain current configuration of location of wall plates and number of sockets in each wall plate.
Pantry shelf. Build a single adjustable shelf in the large space in the pantry. Install pegs to enable adjustment of shelf height. Consult with owner regarding details of solution such as vertical spacing of peg rows and so forth.
Cabinets and cabinet doors. Ensure all cabinets have a uniform stain color and texture. Ensure cabinets are sealed with a high quality sealer. Install high quality European hinges on all cabinet doors.
Counter tops. Replace the full L-shaped section of counter top at the right side of the stove with new quartz material, Caesar stone Carmel #9350. Buff all seams between top surfaces and bull noses. All seams between top surface and bull nose shall be smooth and invisible as much as is reasonable to expect.
All quartz surfaces shall be of uniform color and pattern. If this is not possible due to variations in die lots, replace all counter tops with new material so that all material comes from the same die lot and is of uniform color and pattern. Consult with owner.
Paint interior of all cabinets as specified in section entitled Interior Paint Specification.
Completely cover all appliances, sinks, etc. while doing this work.
Plumbing. Finish installation of plumbing piping and fixtures.
Roman shade. Install Roman shade in kitchen window. Customer purchases.
Appliances. Install all appliances (stave and microwave oven). Contractor purchases all necessary hoses, lines, peripheral accessories such as electrical chords, plugs, male elbow and riser for dishwasher, gas flex line for stove, etc. Customer purchases main appliances.
Dishwasher. Ensure dishwasher is not leaking at host valve.
LIVING ROOM. Do the following work in the living room.
Living room recessed lighting layout, apartment 1. Replace all six (6) recessed light trim with $58 elegant looking trim. Replace existing cans if they do not meet code for heat dissipation, ability to accommodate 350W incandescent bulbs, etc. Consult with owner regarding brand and model. Install two (2) dimmer switches in living room. One dimmer shall control the five (5) living room recessed lights. The second dimmer shall control the single recessed light above the front door entryway.
Light switches. Install a panel of light switches to control exterior lighting that includes porch lights, front entry lights and front building lights. Consult with owner. See section entitled Main Building Exterior for details on exterior lighting.
Patching/painting downstairs, apartment 1. Do the following to touch up apartment 1 downstairs.
Remove acoustic ceiling and top surface applied by first contractor. Consult with owner regarding whether to remove the underlying acoustic ceiling. Float ceiling. Or, just float ceiling. Prime and paint with two coats of paint as specified in Paint Specification section. Apply “orange peel” texturing to ceiling.
Sand all walls to remove all layers of paint applied by first contractor. Patch and prep all walls, smooth surfaces. Prime and paint with two coats of paint as specified in Interior Paint Specification section.
DOWNSTAIRS BATHROOM, APARTMENT 1. Do the following work.
Reposition existing light fixture wiring plate several inches upward from its current location. Consult with customer for precise positioning.
Upgrade electrical socket to GFCI. Install electrical socket wall plate.
Install light fixture. Customer purchases.
Install dimmer switch.
Install commercial grade angle stops for toilet and for sink hot and cold water supply. Reposition sink angle stops to look esthetically pleasing with the pedestal sink selected by customer. Fix tile as necessary after installing angle stops.
Patch walls, prep, prime and paint room with 2 coats of high-quality paint as specified in Interior Paint Specification section.
Install new, quiet, elegant looking, commercial grade bath room ceiling fan. Consult with customer regarding selection.
Install mirror. Customer purchases.
Install new pedestal sink. Install faucet, Moen single-handle, brushed nickel finish, no plate, model 4557. Customer purchases.
Install towel bars and toilet paper holder. Customer purchases.
Install new six-paneled door, painted as specified in Interior Paint Specification section.
UPSTAIRS BATHROOM, APARTMENT 1. Do the following work.
Reposition existing light fixture wiring plate several inches upward; center wiring plate over vanity space. Consult with customer for precise location. Patch, prime and repaint old wiring plate location.
Install new lighting fixture. Customer purchases.
Install dimmer switch.
Replace 2-socket electrical outlet with 4-socket outlet in same location as existing outlet.
Install commercial grade angle stops for toilet and for sink hot and cold water supply.
Install mirror. Customer purchases.
Install new vanity, vanity counter top and vanity sink. Use Caesar stone Carmel #9350 quartz material. Contractor purchases counter top. Customer purchases vanity and sink.
Install new sink faucet, Moen Kingsley single-handle, high arc mini widespread, brushed nickel finish, no plate, model 6102.
Install toilet paper holder; attach to vanity. Customer purchases toilet paper holder.
Install towel bars. Customer purchases.
Build recessed magazine rack in long wall opposite toilet. Consult owner for precise location and details.
Patch walls, prep, prime and paint room with two (2) coats of high-quality paint as specified in Interior Paint Specification section.
Install new door, painted as specified in Interior Paint Specification section.
BEDROOMS, APARTMENT 1. Do the following work.
Install new lighting fixtures. Customer purchases.
Install new dimmer light switches for bedroom light fixtures.
Paint bedroom and closets with primer and 2 coats of paint, matte finish as specified in Interior Paint Specification section.
Install new bedroom and closet doors in master bedroom. Install new bedroom door in small bedroom. If customer's door hinges do not fit, contractor will purchase door hinges. Doors will be painted as specified in Interior Paint Specification section.
AUDIO/VISUAL (A/V), TELEPHONE, INTERNET CONFIGURATION AND WIRING. Install all A/V, Internet and telephone wiring as follows.
Cable TV, satellite TV and closed-circuit TV (CCTV) security system wiring. All wiring, including cables, wires and patch chords shall consist of RG6Q (RG6 Quad) cable, connected to F-type connectors in wall plates.
Internet wiring. Use Cat 6A compliant (EIA/TIA Cat 6A) cable, connected to RJ-45S wall plate jacks for all Internet wiring, including cables, wires and patch chords.
Telephone wiring. Use high-quality, shielded, twisted pair phone wire, connected to RJ-14C/RJ-14W powered jacks in wall plates for all telephone wiring.
Kitchen – One (1) wall plate containing two (2) RJ-14C/RJ-14W powered jacks, one (1) RJ-45S jack and one (1) F-type connector in same location as current telephone wall plate in kitchen.
Downstairs living room – two (2) wall plates each containing three (3) F-type connectors, one (1) RJ-14C/RJ-14W powered phone jack, one (1) RJ-45S Cat 6A compliant jack. Wall plates shall be in same location as existing wall plates.
Large bedroom – one (1) wall plate containing three (3) F-type connectors, one (1) RJ-45S jack, one (1) RJ-14C/RJ-14W telephone jacks.
Small bedroom – one (1) wall plate containing three (3) F-type connectors, one (1) RJ-45S jack, one (1) RJ-14C/RJ-14W powered telephone jacks.
Cable modem and wireless router accommodation. The recessed panel area shall further accommodate a large-sized cable modem and wireless router.
Signal supply route. Signal supply wiring for cable TV, Internet, internal computer networking and telephone lines shall run from the east side of the house, under the house in the crawl space, and up into the downstairs coat closet. Internal wiring shall be distributed from the downstairs coat closet to the locations throughout the house specified above. The coat closet will accommodate a universal routing configuration of cable TV, satellite TV, Internet and telephone lines. The universal routing configuration installation will follow the owner's design.
Seal, plaster, prime and paint old phone jacks in bedrooms.
GENERAL APARTMENT 1 SPECIFICATIONS.
New light dimmer switches. Install light dimmer switches for the following light fixtures:
Living room recessed lights
Front door entry recessed light
Kitchen nook chandelier
Downstairs bathroom
Downstairs bathroom nook
Upstairs bathroom
Bedrooms
New light switches. Install new light switches throughout. Use switches that match dimmer switches. Switches can be plain switches (no dimmers) except as specified immediately above.
Interior doors. Replace all interior doors (bathrooms, bedrooms, closets), with new product. Install solid core doors with six (6)-panel relief pattern such as a rectangular relief with mitered edged. Square all internal doors so they close and latch perfectly and smoothly.
Install new brushed nickel door hinges for all internal doors. Customer has purchased hinges. If hinges are not correct, contractor will purchase correct hinges.
Door and closet hardware. Replace all interior door knobs and clasps with new hardware. Customer purchases.
Install new high-quality, elegant looking hinges and magnetic clasps in all hallway closets.
Replace all closet pulls with new hardware. Customer purchases.
Front door and casings. Contractor purchases and installs new fiberglass door and door hardware. Install new casings and jambs if necessary. Door will have a security lens (“peep” hole), half-moon “fan light” decorative glass design and a bronze kick plate. Consult with owner. Customer will make final selection after consultation with contractor.
Paint door the color of the new cap bricks atop the brick wall that forms a perimeter around the front garden.
Flooring, apartment 1. Complete installation of flooring at gaps between laminate wood and tile flooring, thresholds, etc.
Stairs. Fix bottom stair so that front door can open completely without hitting stair.
Sand stairs; stain with existing stain color; seal. Sand again; stain; seal. Use high-quality, stain and sealer. Stairs should be stained to match the color of the flooring as closely as possible.
Paint stair risers as specified in Interior Paint Specification section. Seal with high-quality sealer (lacquer?) or other appropriate protective layer to protect risers again shoe scuffs and marking.
Staircase banister. Remove banister. Sand completely, prime and add 2 coats of high-quality paint. Reinstall banister after stair flooring is installed.
Base boards. Install new base boards throughout downstairs and upstairs. Use Superior Molding model #HB20-44. See section Interior Paint Specification for paint details.
Quartz shelf and cabinet in downstairs bathroom nook. Build or buy and install a built-in cabinet in the downstairs bathroom nook, along the wall shared with the kitchen. The cabinet shall be 12” deep x 36” tall spanning the length of the wall. The cabinet top shall be quartz, Caesar stone Carmel #9350, 12” deep along the full length of the cabinet, with a half-round bull nose. The cabinet shall have legs approximately three inches (3”) high and shall be constructed from some tasteful quality-looking material, such as a thin veneer of wood over MDF. The cabinet should be built such that the electrical outlets on the wall above the base board can be accessed easily for standard sized plugs. The cabinet finish shall be the same as that of the kitchen cabinetry.
Windows reveals. Retrofit all window reveals in apartment 1 so that they done according to standard practice and are perfectly square and level.
Ensure all windows throughout building are sealed properly at frame.
Windows and sliding glass doors. Before completion of job, remove all windows from their frames for cleaning. Replace any broken or disintegrated wheels and rollers. Clean edges of windows and frames completely and thoroughly. There should be not even a single spec of dirt or dust. Clean railings so windows slide smoothly. Apply suitable and appropriate lubricant to bottom of frames so windows slide smoothly without abrasion. Frames and windows shall look as clean as the moment they were delivered.
Smoke detectors. Install AC-powered smoke detectors in all rooms as required by the building code. Preferred location is above bedroom doors.
Plumbing. All plumbing hoses shall be high-quality metal-braided hoses.
Door bells. Install new wireless door bells. Install buttons on brick pillars as specified by owner. Install bell unit in kitchen, above kitchen window, in the position specified by owner. Consult with owner for exact solution and details.
INTERIOR PAINT SPECIFICATION.
All painting shall consist of sanding existing surfaces to remove all paint applied by previous contractor. Apply quality primer coat and 2 coats of latex paint.
Color selection should match as closely as possible to colors below. Contractor shall match wall color with color of paint card (paint chip). If necessary, contractor shall select a different shade or hue in the same color family to compensate for the variation between the cardboard paint card and the more glossy, brighter color of the paint on the wall.
All ceilings: Behr “White” (1852), flat finish.
Kitchen ceiling: Behr “White” (1852), sateen finish.
All internal doors and door casings (bedroom, bathroom, closet doors) and cabinets and book shelves: Behr “Swiss Coffee” (1852), semi-gloss or sateen finish.
Half-height cabinet and wall behind half-height cabinet in bathroom nook: “Swiss Coffee” (1812).
Wall containing bathroom door and wall above half-height cabinet: “Cozy Cottage” (740C-2).
Base boards and stair risers: Behr “Swiss Coffee” (1812), semi-gloss finish.
Kitchen walls: Behr “Winter lake” (550F-5) sateen finish.
Kitchen cabinet interiors: Behr “White” (1852), sateen finish.
Living room, bedrooms, hallways, closet interior walls, downstairs built-in book shelf, laundry room: Behr “Cozy Cottage” (740C-2), flat finish.
Living room accent walls (wall adjacent to kitchen and west wall adjacent to driveway): Behr “Winter lake” (550F-5) matte finish.
Bathroom walls: Behr “Winter lake” (550F-5), sateen finish.
Tile grout color: <tile grout color>
MISCELLANEOUS.
Wall plates for light switches in living room, bedrooms and bathrooms shall be dimmers, almond color, glossy finish.
# APARTMENT 2 INTERIOR
HVAC SYSTEM. Do the following work on the HVAC system.
HVAC system maintenance. Test HVAC system and verify that is is functioning properly, and, if not, bring it to proper functioning condition. Pressure test lines and ducting. Perform two-year (2year) scheduled maintenance.
HVAC air return air filter. Install SpaceGuard air filter or brand and model filter of equivalent quality. The filter installed should be the kind that lasts for six (6) months.
Programmable thermostat. Install a programmable thermostat in the position specified by owner. Position the location of the new thermostat approximately one foot (1') to the right of its current position. Run appropriate wiring from the actual HVAC unit to the thermostat to provide power to the thermostat (low-voltage 24V electrical supply) if such wiring is not already in place. Run the line in the wall, directly down from the attic in line with the thermostat's location. Owner purchases thermostat.
KITCHEN, APARTMENT 2. Do the following work.
Recessed lights. Install two six-inch (6”) recessed lights in kitchen to mirror the configuration and location of the recessed lights in the apartment 1 kitchen. Use $58 elegant looking trim. Consult with owner regarding final selection and finish.
Kitchen sink pendant light fixture. Install pendant light fixture above kitchen sink. Customer purchases.
Dining room nook chandelier. Move existing chandelier fixture wiring plate about 8” - 12” from its present position. Consult owner for precise location of new wiring plate. Install new chandelier above nook. Customer purchases.
Electrical wall plates and sockets. Upgrade all existing electrical wall plates and sockets to new equipment.
GFCI wall plates, sockets and circuits. Install GFCI-compliant wall plates and circuits where necessary to comply with building code. Retain current configuration of location of wall plates and number of sockets in each wall plate.
Dedicated electrical circuits. Wire dedicated circuits for microwave, dishwasher, and any other appliances as required by code.
GFCI wall plates, sockets and sockets. Install GFCI-compliant wall plates throughout kitchen. Mirror the apartment 1 configuration in regards to the location of wall plates and number of sockets in each wall plate as specified immediately following:
Install a 4-socket GFCI electric wall plate at the end of the counter top closest to the sliding patio door, mirroring the type and position of counterpart in the apartment 1 kitchen.
Install a 2-socket GFCI electrical wall plate to the left of the sink, mirroring the type and position of the counterpart in the apartment 1 kitchen.
Install a 2-socket GFCI electric socket and plate at the back of the dishwasher space, under the kitchen counter top.
Install wiring and a 2-socket GFCI electrical wall plate for a dedicated electric circuit for the microwave oven at the back of the new microwave enclosure in the pantry. See paragraph entitled “Microwave enclosure” below.
Pantry shelf. Build a single adjustable shelf in the large space in the pantry like that in apartment 1. Install pegs to enable adjustment of shelf height. Consult with owner regarding details of solution such vertical spacing of peg rows and so forth.
Microwave enclosure. Build a microwave oven enclosure/shelving and frame for microwave inside existing kitchen pantry to match that in apartment 1. The microwave oven shall be “exposed” (no doors to enclose space). Refinish (stain and seal) interior wood. Change pantry doors to match those in apartment 1. The two doors shall close the pantry shelves that will be above and below the microwave oven frame, respectively).
Cabinets and cabinet doors. Lightly sand and prep all kitchen cabinets. Stain cabinets so that the color and texture are as close as possible to the apartment 1 kitchen cabinets. Seal with a high quality sealer. Do all this work with cabinets in place (do not remove cabinets).
Replace existing cabinet doors with new oak doors to match the oak wood kitchen cabinet doors in apartment 1. For each cabinet, ensure that left and right side doors match in wood grain pattern (as much as possible), stain color and finish.
Install top cabinet molding at junction between cabinets and ceiling just like that in apartment 1 in regards to grain, quality, dimensions, style, etc. Install top cabinet molding exactly like that in apartment 1 kitchen.
Install new European hinges on all cabinetry.
Paint interior of all cabinets as specified in section entitled Interior Paint Specification.
Install new cabinet hardware (knobs). Install elegant rubber door stops to prevent cabinet doors and cabinets from damage upon contact. Customer purchases knobs.
Dishwasher space. Cut space in existing cabinetry at right side of sink below counter top for the dishwasher. Lay as many pieces of one-inch (1”) plywood as necessary to form the new kitchen counter top base for all counter tops at the level suitable to accommodate the dishwasher with tile beneath it. Counter top level must be raised to accommodate dish washer. Ensure space is enough to comfortably fit dish washer.
The floor beneath the dishwasher shall be tiled like the rest of the kitchen. That is, contractor shall accurately design the height of the counter top to consider the raised height of the floor after the tile installation., the size of the counter top bull nose needed to hide the plywood beneath the counter top and the feasibility of a large bull nose, esthetic appeal of the bull nose, and so forth.
Cookie sheet and spice rack. Build a cookie sheet cabinet at left side of new 30” stove like that in apartment 1. The cabinet will fill the space to the left of the new stove, and shall extend from the floor to the underside of the counter top, minus any space needed for framing. Wood selection and stain color shall match existing cabinetry in apartment 1. Cabinet hinges shall be provided by contractor.
Build a spice/utility cabinet in kitchen, adjacent to oven, on opposite side of “cookie sheet” cabinet like that in apartment 1. The cabinet shall extend vertically from the floor to the underside of the kitchen counter top. Rack shall have two or three levels of shelving inside. Consult with owner. Front shall be stained and sealed to match the rest of the cabinetry. Cabinet hinges shall be provided by contractor.
Sink. Install new under mount double kitchen sink, Ferguson Pro-flo 18-gauge brushed stainless steel double sink, dimensions 32 1/4” W x 18 1/2” D, model PFUE206, item #PFUE206. Or, install different brand and model with the same dimensions and equivalent quality, finish and gauge.
Counter tops. Install new quartz counter tops, Caesar stone Carmel #9350, with bull nose edge like that in apartment 1. Buff all seams between top surfaces and bull noses. All seams between top surface and bull nose shall be smooth and invisible as much as is reasonable to expect.
All quartz surfaces shall be of uniform color and pattern and come from the same die lot.
Plumbing. Install new kitchen sink faucet, Moen Extensa, model 7560SL, stainless steel finish, single handle kitchen faucet, item #M7560SL.
Install dish washer air gap, Moen air gap, item #MB139232.
Install sink soap/lotion dispenser, Moen brushed nickel finish, item #MB132992.
Install new garbage disposal, disposal flange, Moen disposal flange, brushed nickel finish, item #MB132975. Install disposal under left side sink basin.
Wall tile. Install new wall tile. Use Travertino beige “six inch” (6” x 6”) porcelain tile like that in apartment 1. Customer purchases wall tile.
Floor tile. Install new tile kitchen floors:. Use Travertino noche “twelve-inch” (12)” square porcelain tile like that in apartment 1. Customer purchases floor tile.
Roman shade. Install Roman shade in kitchen window. Customer purchases.
Appliances. Install appliances (stove and microwave oven). Contractor purchases all necessary hoses, lines, peripheral accessories such as electrical chords, plugs, male elbow and riser for dishwasher, gas flex line for stove, etc. Customer purchases main appliances.
LIVING ROOM. Do the following work in the living room.
Living room recessed lighting layout, apartment 2. Install five (5) six-inch (6”)- diameter recessed lights, 12V cans with standard socket threads, in living room main area just as in apartment 1. Use $58 elegant looking cans and trim. Install one (1) 6” diameter can under front door entry.
Install two (2) three-inch (3”) diameter halogen lights in “nook” near downstairs bathroom. The selection, layout and design will be precisely like that in apartment 1.
Electrical fixtures shall accommodate dimmable compact fluorescent bulbs. Install two (2) dimmer switches in living room. One dimmer shall control the five (5) living room recessed lights. The second dimmer shall control the single recessed light above the front door entryway.
Install $58 elegant looking recessed light cans and trim for all recessed lights in living room, front door entry and bathroom nook. Customer selects cans and trim.
Light switches. Install a panel of light switches to control exterior lighting that includes porch lights, front entry lights and front building lights. Consult with owner. See section entitled Main Building Exterior for details on exterior lighting.
DOWNSTAIRS BATHROOM, APARTMENT 2. Do the following work.
Reposition existing light fixture wiring plate. Consult with customer for precise location.
Upgrade all electrical sockets to GFCI.
Install new commercial grade angle stops for toilet and sink hot and cold water supply. Reposition sink angle stops to look esthetically pleasing with the pedestal sink selected by customer. Leave enough room for potentially wider pedestal to be installed in the future.
Patch walls, prep, prime and paint room with 2 coats of high-quality paint as specified in Interior Paint Specification section.
Tile walls like those in apartment 1 downstairs bath room. Use cement, not backer board.
Tile floor like that in apartment 1 downstairs bathroom. Customer purchases tile.
Install new, quiet commercial grade bath room ceiling fan. Customer will specify selection.
Install new lighting fixture. Customer purchases.
Install dimmer switch.
Install mirror. Customer purchases.
Install new pedestal sink. Customer purchases.
Install new pedestal sink faucet, Moen single handle lavatory faucet with drain assembly, brushed nickel finish, item #M457BN.
Install towel bars and toilet paper holder. Customer purchases.
Install new toilet. Customer purchases.
UPSTAIRS BATHROOM, APARTMENT 2. Do the following work.
Remove existing shower doors. Demolition old tile.
Re-tile shower/tub area using Travertino beige “six-inch” (6” x 6”) porcelain tile. Use cement wall, black paper and wire mesh, not backer board. Build soap/shampoo nooks like those in apartment 1 bath tub.
Install bath tub fixture, Moen Moentrol three-function transfer valve trim, model 4111.
Install bath tub faucet, Moen Kingsley brushed nickel finish 3-function transfer valve, item #MT4111BN, model M3330. Raise shower head height to same height as that in apartment 1. Consult with owner for precise location.
Add anti-slip surface as is apartment 1 bath tub. Material shall be installed such that the pattern is perfectly symmetrical and centered along the center line of the tub. Discuss pattern with owner. Possible patterns are chevron design, hashed lines, and so forth.
Reposition existing light fixture wiring plate and center over vanity space. Patch, prime and repaint old wiring plate location. Consult with customer for precise location.
Upgrade all electrical sockets to GFCI where required by code.
Install commercial grade (durable and attractive) angle stops for toilet and for sink hot and cold water supply.
Patch walls, prime and add 2 coats of paint as specified in Interior Paint Specification section.
Install new toilet. Customer purchases.
Install new lighting fixture. Customer purchases.
Install dimmer switch.
Replace 2-socket electrical outlet with 4-socket outlet in same location as existing outlet.
Install mirror. Customer purchases.
Install new vanity, vanity counter top and vanity sink. Use Caesar stone Carmel #9350 quartz material. Contractor purchases counter top. Customer purchases vanity and sink.
Install new sink faucet, Moen Kingsley single-handle, high arc mini widespread, brushed nickel finish, no plate, model 6102.
Install toilet paper holder per owner's instructions. Customer purchases toilet paper holder.
Build recessed magazine rack in long wall opposite toilet. Consult owner for precise location and details.
Install towel bars. Customer purchases.
Install new porcelain tile floors using Travertino noche “twelve inch” (12”) tile like that in apartment 1.
Install new door, painted as specified in Interior Paint Specification section.
BEDROOMS, APARTMENT 2.
Install new lighting fixtures. Customer purchases.
Install new dimmer light switches for bedroom light fixtures.
Paint bedroom and closets with primer and 2 coats of paint, matte finish as specified in Interior Paint Specification section.
Install new bedroom and closet doors in master bedroom. Install new bedroom door in small bedroom. If customer's door hinges do not fit, contractor will purchase door hinges. Doors will be painted as specified in Interior Paint Specification section.
Build soffit in small bedroom closet to close-off the HVAC system ducting.
AUDIO/VIDEO (A/V), TELEPHONE, INTERNET CONFIGURATION AND WIRING. Install all A/V, Internet and telephone wiring as follows.
Cable TV, satellite TV and closed-circuit TV (CCTV) security system wiring. All wiring, including cables, wires and patch chords shall consist of RG6Q (RG6 Quad) cable, connected to F-type connectors in wall plates.
Internet wiring. Use Cat 6A compliant (EIA/TIA Cat 6A) cable, connected to RJ-45S wall plate jacks for all Internet wiring, including cables, wires and patch chords.
Telephone wiring. Use high-quality, shielded, twisted pair phone wire, connected to RJ-14C/RJ-14W powered jacks in wall plates for all telephone wiring.
Kitchen – One (1) wall plate containing two (2) RJ-14C/RJ-14W powered jacks, one (1) RJ-45S jack and one (1) F-type connector in same location as current telephone wall plate in kitchen.
Downstairs living room – two (2) wall plates each containing three (3) F-type connectors, one (1) RJ-14C/RJ-14W powered phone jack, one (1) RJ-45S Cat 6A compliant jack. Wall plates shall be in same location as existing wall plates.
Large bedroom – one (1) wall plate containing three (3) F-type connectors, one (1) RJ-45S jack, one (1) RJ-14C/RJ-14W telephone jacks.
Small bedroom – one (1) wall plate containing three (3) F-type connectors, one (1) RJ-45S jack, one (1) RJ-14C/RJ-14W powered telephone jacks.
Cable modem and wireless router accommodation. The recessed panel area shall further accommodate a large-sized cable modem and wireless router.
Signal supply route. Signal supply wiring for cable TV, Internet, internal computer networking and telephone lines shall run from the east side of the house, under the house in the crawl space, and up into the downstairs coat closet. Internal wiring shall be distributed from the downstairs coat closet to the locations throughout the house specified above. The coat closet will accommodate a universal routing configuration of cable TV, satellite TV, Internet and telephone lines. The universal routing configuration installation will follow the owner's design.
Seal, plaster, prime and paint old phone jacks in bedrooms.
GENERAL APARTMENT 2 SPECIFICATIONS.
Interior electrical sockets. Install new electrical sockets and wall plates throughout living unit to replace existing sockets and wall plates.

Interior light fixtures. Install all interior light fixtures, including kitchen, kitchen nook, downstairs coat closet, stairway landing, bedrooms, closets, etc. Customer purchases.
Light switches in coat closets, apartment 2. Install light switch in downstairs coat closet and in both master bedroom closets. Consult with customer for precise location.
New light dimmer switches. Install dimmer switches for the following light fixtures:
Living room recessed lights
Front door entry recessed light
Kitchen nook chandelier
Downstairs bathroom bookshelf picture lights
Downstairs bathroom
Upstairs bathroom
Bedrooms
New light switches. Install new light switches throughout.
Interior doors. Replace all interior doors (bathrooms, bedrooms, closets) with new product. Install solid core doors with six (6)-panel relief pattern such as a rectangular relief with mitered edged. Square all internal doors so they close and latch perfectly and smoothly.
Install new brushed nickel door hinges for all internal doors. Customer has purchased hinges. If hinges are not correct, contractor will purchase correct hinges.
Door and closet hardware. Replace all interior door knobs and clasps with new hardware.
Install new high-quality, elegant looking hinges and magnetic clasps in all hallway closets.
Replace all closet pulls with new hardware Customer purchases.
Front door and casings. Contractor purchases and installs new fiberglass door and door hardware. Install new casings and jambs if necessary. Door will have a security lens (“peep” hole), half-moon “fan light” decorative glass design and a bronze kick plate. Consult with owner. Customer will make final selection after consultation with contractor.
Paint door the color of the new cap bricks atop the brick wall that forms a perimeter around the front garden.
Downstairs flooring, apartment 2.
Screw down existing plywood. Install an additional one-half inch (1/2”) layer of plywood and screw down before installing laminate flooring (I have the wood screws). Float all floors. Install new Eternity Floors, Sapphire line, Red Ancient Pine, model VG1052, 12mm thick laminate flooring. Make the final level of the laminate wood flooring the same height as the new kitchen tile flooring and the downstairs bathroom tile flooring, as was done in apartment 1. Ensure that the laminate wood flooring abuts the tile and that the two surfaces are flush and level and are the same height.
Install new Eternity Floors, Sapphire line, Red Ancient Pine, model VG1052, 12mm thick laminate wood flooring throughout interior, including dining room nook, living room, downstairs coat closet, bedrooms, bedroom closets and upstairs hallway and landing.
Upstairs flooring, apartment 2.
Screw down existing plywood. Install an additional one-quarter inch (1/4”) or one-half inch (1/2”) layer of plywood throughout bedrooms, closets and hallway and screw down before installing laminate flooring. Float floors. Install new Eternity Floors, Sapphire line, Red Ancient Pine, model VG1052, 12mm thick laminate flooring. Make the final level of the laminate wood flooring the same height as the new upstairs bathroom tile flooring, as was done in apartment 1. Ensure that the laminate wood flooring abuts the tile and that the two surfaces are flush and level and are the same height.
Stairs. Install oak wood stairs just like apartment 1. Sand stairs; stain; seal. Sand again; stain; seal. Use high-quality, stain and sealer. Stain stairs to be like that in apartment 1. Stairs should be stained to match the color of the flooring as closely as possible.
Paint stair risers as specified in Interior Paint Specification section. Seal with high-quality sealer (lacquer?) or other appropriate protective layer to protect risers again shoe scuffs and marking.
Staircase banister. Remove banister. Sand completely, prep, prime and add 2 coats of high-quality black paint like color of apartment 1 banister. Reinstall banister after stair flooring is installed.
Base boards. Install new base boards throughout. Use Superior Molding model #HB20-44. See section Interior Paint Specification for paint details.
Living room built-in bookshelf. Install built-in bookshelf in nook outside of downstairs bathroom. Bookshelf will extend to ceiling and contain three compartments. Bottom will consist of cabinets (with doors). Consult with owner or interior designer for precise details, dimensions, measurements, etc.
Stain bookshelf per interior decorator's specification. Seal with high-quality, high protection sealer.
Windows and sliding glass doors. Replace 1 window, 95” x 46” on east wall near breakfast nook in apartment 2. Break stucco and install new window (not “replacement” window). Customer purchases window. Redo scratch coat, brown coat and paint when complete exterior paint job is done.
Before completion of job, remove all windows from their frames for cleaning. Replace any broken or disintegrated wheels and rollers. Clean edges of windows and frames completely and thoroughly. There should be not even a single spec of dirt or dust. Clean railings so windows slide smoothly. Apply suitable and appropriate lubricant to bottom of frames so windows slide smoothly without abrasion. Frames and windows shall look as clean as the moment they were delivered.
Smoke detectors. Install AC-powered smoke detectors in all rooms as required by the building code. Preferred location is above bedroom doors.
Acoustic ceilings, apartment 2. Remove existing acoustic ceiling in living rooms. No asbestos is present in the ceilings. Apply “orange peel” texture over plaster patch.
Plumbing. All plumbing hoses shall be high-quality metal-braided hoses.
Door bells. Install new wireless door bells. Install buttons on brick pillars as specified by owner. Install bell unit in kitchen, above kitchen window, in the position specified by owner. Consult with owner for exact solution and details.
INTERIOR PAINT SPECIFICATION.
All painting shall consist of sanding existing surfaces, using a primer coat and 2 coats of latex paint.
Color selection should match as closely as possible to colors below. Contractor shall match wall color with color of paint card (paint chip). If necessary, contractor shall select a different shade or hue in the same color family to compensate for the variation between the cardboard paint card and the more glossy, brighter color of the paint on the wall.
All ceilings: Behr “White” (1852), flat finish.
Bathroom ceilings: Behr “White” (1852), sateen finish.
All internal doors and door casings (bedroom, bathroom, hallway linen closets, closet doors), downstairs built-in book case: Behr “Swiss Coffee” (1852), semi-gloss finish.
Built-in book case and wall behind built-in book case: “Swiss Coffee” (1852), matte finish.
Base boards, stair risers: Behr “Swiss Coffee” (1812), semi-gloss finish.
Kitchen walls and wall containing sliding glass door: Behr “Cozy Cottage” (740C-2), sateen finish.
Kitchen cabinet interiors: Behr “White” (1852), sateen finish.
Living room, bedrooms, hallways, closet interiors, laundry room: Behr “Cozy cottage” (740C-2), flat finish.
Living room accent walls (eastern most long wall): Behr “Cup of Cocoa” (ICC-52) matte finish.
Bathroom walls: Behr “Cozy Cottage” (740C-2), sateen finish.
Tile grout color: <tile grout color>
Accent color:
1. Warm Nutmeg, ICC-71
2. Cup of Cocoa, ICC-52 (more contrast) or
3. Comforting, ICC-42 (less contrast)
Miscellaneous. Install almond color, glossy finish light switch plates all plates in living room, bedrooms and bathrooms.
# MAIN BUILDING EXTERIOR
GAS SUPPLY. Do the following work related to the building's natural gas supply.
External gas supply line. Replace rusted external gas pipes located in breezeway on east side of building. Or, repaint pipes if this is sufficient to stop rusting and avoid compromising the integrity of the pipes.
Gas meter installation and connection. The Southern California Gas Company will install the new gas meter (third meter) servicing the back structure.
Seismic automatic gas safety valves. Install two (2) new seismic automatic gas safety valves on the two (2) gas meters that currently have no safety valve. Install valves like the existing one. Install each valve “vertically” on the “house side” of its respective gas meter. Install per owner's instructions (especially in regards to the existing piping).
WATER SUPPLY. Do the following work related to the building's water supply.
Water heater enclosure doors and plumbing trap doors. Install new water heater closet doors. Doors should be stiff and durable and dent resistant. Apply primer and two coats of durable, quality paint to match color of building paint. Contractor purchases and installs latch (without lock) to water heater enclosure doors.
Water heaters crossed gas lines. Fix crossed gas lines. This work involves removing one flex gas line from the existing apartment 2 water heater and reconnecting it to the existing apartment 1 water heater.
Existing hose bib on east side breezeway. Shorten by about two to three inches (2”–3”) the water pipe (faucet) in the breezeway underneath the electrical panels to avoid anyone tripping over it. Consult with owner for details.
ELECTRICAL SUPPLY AND WIRING. Do the following work related to the building's electrical supply.
Electrical panels and conduit piping. Straighten conduit pipe housing cable line coming from pole so it is perfectly vertical, not bent. At end of job all residue from stucco, paint, etc. should be completely removed from panels, conduit piping, wiring, etc.
Electrical wiring for low-voltage security system. Add wiring for a 9-camera CCTV security system (Run wires to 9 camera locations to be specified by owner). Wiring shall include both signal and power wiring (for electrical power to cameras). Consult with owner on precise location of cameras.
The security recording system itself shall support storing of 30 days of 24x7 recording of 1080p high-definition (HD) resolution. Owner prefers a digital, Linux-based continuous recording system. Discuss solution with owner, including wired or wireless, precise locations of cameras, location of video recording equipment, interior wiring required, etc. Install all wiring and video cameras.
Thread all signal cables and electrical power cables to power cameras inside building walls and run them down to the building crawl space. In crawl space, all signal cables shall be marshaled into a single metal conduit pipe. The conduit pipe shall run in the crawl space to the north-west corner of the main building. It will tunnel under the patio cement and surface to the left of the laundry room door where the conduit will enter the garage. Conduit shall be positioned so as to cause the least amount of obstruction in the crawl space. Please see paragraph entitled “Electrical wiring for low-voltage security system” in section entitled Back structure in this document.
Customer purchases security cameras.
Exterior lighting fixtures. Install exterior light fixtures. Customer purchases. Raise level of wiring for light fixtures (back patio lights, apartment front door lights) by an amount indicated by owner.
Exterior electrical outlets. Install seven (7) new, corrosion-resistant, 2-socket electrical socket assemblies (wall plates) with weather-proof, water-proof covers on the outside of the main building. The units shall be installed flush with the building stucco. The installation locations are as follows:
Apartment 1. The wiring for four (4) of the outlets outside apartment 1 has already been done; only the assemblies for these need to be replaced with the kind that is flush with the stucco.

Apartment 2. The remaining three (3) outlets shall be done as part of the apartment 2 work. Locations of boxes are Consult customer for precise locations:
One (1) electrical outlets in patio on north wall (facing patio), one beneath each apartment kitchen.
One (1) electrical outlets on south wall (facing street), one each near stairs leading down to left and right from porch.
One (1) electrical outlet on east wall of main dwelling in breezeway.
Brick pillar cap stones. Install a cap stone atop each of the four (4) brick pillars at the front entryway. Owner shall make selection.
CRAWL SPACE ACCESS AND VENTILATION.
Crawl space entry screen. Install new screen to cover building crawl space opening.
Crawl space entry well cover. Install a solid (no holes) steel protective/safety cover plate over the building crawl space entry well. The cover should fit over and around the raised cement frame of the crawl space well. The steel shall be strong enough to support 300 lbs. with no deformation, movement, buckling, etc. The material should be rust proof or have a baked-on rust proofing.
Building vent grill covers. Replace torn or worn mesh with new mesh for all building crawl space vents.
EXTERIOR SATELLITE TV, CABLE TV, INTERNET AND TELEPHONE.
All A/V wiring for satellite TV, cable, Internet services and telephone lines should be in a durable, high-quality, flexible, multi-wire sheath. Where possible, run “integrated” or “structured” sheath to accommodate wires for all services and functions accessed from that destination.
Run all cables from the east side of the house (cable box) in building crawl space to the distribution points in each apartment (downstairs coat closets in each apartment). For details on inside wiring, please see the specifications for apartment 1 and 2.
Cable TV and Internet wiring. Run RG6Q cable A/V wiring for cable TV and Internet service from the signal supply pole down to the cable box on the east side of the building. Attach all cables correctly in the cable box on the east wall in building breezeway.
Satellite TV antenna platform. Bolt an additional 2” x 6” or thicker fascia board to the building's east side fascia board to which to attach satellite TV dishes. All satellite dishes will be bolted to this board to avoid damaging the building's main fascia boards. The criteria for the solution are longevity of building integrity, durability and reliability. The new fascia board shall be primed and painted with 2 coats of quality, exterior latex paint. Consult with owner regarding the best solution.
Satellite TV wiring. Install two (2) wall plates with two (2) F-type connectors each near the top of the east wall below fascia board to serve as a connection point for the signal feed from the satellite dishes. Install appropriate connectors with weather-proof caps. Run RG6Q cable in weather-proof conduit from the wall plates down to a distribution box on the east wall of the building.
Cable box. Re-attach cable box to wall. The box should be secure and should never move or detach from wall.
BUILDING FRONT DECORATIVE PIECE. Install a decorative piece on the south facing wall (front wall facing street) of the main building. Owner purchases decorative piece.
STUCCO AND EXTERIOR PAINT. The following work will be done.
Repair stucco (scratch coat, brown coat, color coat) around window that will be replaced (apartment 2 east wall).
Repair/replace damaged stucco in all areas identified by customer if necessary, if stains cannot be completely removed. Remove and redo the bottom foot of stucco around the main building on the west and north sides if necessary. Remediate any stucco that is not drying. Repair stucco surrounding electrical panels and telephone box.
Paint entire building stucco with two (2) coats of paint to match existing color coat (MERLEX brand “cafe mocha”) per approval of customer or interior decorator. Final product shall have uniform color and visual texture everywhere. Wait a minimum of three (3) days between applications of stucco coats or paint coats to allow time for thorough drying.
RAIN GUTTERS. Remove rain gutter conduit under balcony. Add a vertical conduit on the north side of the balcony. Gutter should come straight down to the driveway like the gutter conduit near the apartment 1 sliding glass patio door. Install new seamless baked, painted aluminum 6” gutters.
WROUGHT IRON DRIVEWAY GATE, FENCING AND RAILING.
Driveway gate doors. Adjust driveway gate wrought iron doors per owner's specification. Both doors must be installed and spaced properly and be able to open smoothly and without obstruction in all temperatures throughout the year without touching or abrading against each other. Ensure driveway doors are installed square and level, have flush tops and bottoms, are at the same height and open and close smoothly.
Automatic driveway gate openers. Install two electric, remote-controlled gate openers. Connect one to each of the left and right driveway gate doors. Install one motor in the dirt strip near the cinder block wall. Install the second motor in the left side front garden dirt near the front-left corner, depressed into the dirt as much as possible. Install high-quality, durable, reliable remote-controlled motors.
Electrical supply for driveway gate openers. Run electrical power supply wiring from the garage to the gate motor near the cinder block wall. Run electrical power supply wiring from the main house to the motor in the left side front garden near the brick wall.
House all wiring in metal conduit, run in the dirt strip bordering the driveway on the west side, adjacent to the cinder block wall. The electrical circuit supplying power shall be on the “house meter”.
Install door stops (for example protective rubber bumpers on brick or door) to avoid damage to gate doors, cinder block wall or brick wall. Consult with owner regarding options. Owner shall choose final solution.
Wrought iron fence. Remove all signs of rust on all existing wrought iron fencing and doors. Power wash all wrought iron. Paint all wrought iron, including balcony railing, with special paint that bonds with rust. Then paint with two (2) coats of durable, high-quality weather-proof, exterior black paint.
Door locks for wrought iron doors. Install a high quality, security lock on the main entrance wrought iron door. Customer makes final selection.
Front porch stairs hand railing. Install the following wrought iron hand railing for the front porch steps. Wrought iron will be the same quality as the new driveway doors, 3/16 gauge, with primer baked on at the factory and painted with two (2) coats of high-quality, durable weather-proof black paint.
Install a single wrought iron hand rail in the middle of the porch, spanning the top three steps closest to the top of the porch itself.
Install wrought iron hand rails for the stairs leading down from the left and right side of the porch. The rails shall be bolted to the building front, angled per the owner's instructions.
All of the above wrought iron shall have the same design as the existing static wrought iron atop the existing front brick wall. Consult with owner for approval and clarification as necessary.
Hand railings for rear doors of apartment units. Install a vertically oriented wrought iron hand rail adjacent to each unit's rear sliding glass patio door. Install the hand rail on the “inside” of the sliding glass door, that is, between the door and the buildings center.
REDWOOD FENCE. Patch existing redwood fence along full east wall (6 foot high, with 2 foot high lattice on top). Ensure all spots are sealed, primed and painted like existing paint. Add one additional coat of sealer or weather-proofing.
Fix redwood fence gate latch. Currently gate is difficult to open; latch is too tight. Add wire “string” threaded through a hole to allow gate to be opened from front yard. Consult owner for precise details.
FRONT PORCH AND PORCH OVERHANG. Fix beam that supports porch overhang so it is square. Fix capitols of existing columns so they are level, sealed, and square relative to the support structure. Fix area where beam adjoins stucco to make a more esthetically pleasing design. Add wood to top of column capitols on all four sides so that the edges of the capitols are flush with the wood atop the capitol all the way to the bottom of the overhang. On outside edges, add a finish surface to make the material uniform. Discuss exact solution, material choice, structure, etc. with owner.
Paint pillars (columns and capitols) as specified below under Internal Paint heading.
Cover porch, stairs and walkway with jagged-edged 10mm thick multi-colored slate to be selected by customer.
FRONT YARD WALKWAY SLATE. Install 10mm thick multi-colored walkway slate along the ground in the front yard of the building, leading from the porch to the side edges of the yard. The slate shall extend from the bottom porch step to the brick work adjacent to driveway on the left side and to the far edge of the redwood fence door on the right side of the porch. Slate shall be installed adjacent to building wall. Walkway shall be 30” wide. Consult with owner regarding material selection, placement, etc.
FRONT GRASS STRIP PAVING STONES. Replace grass with the same Olsen stone color scheme and pattern used in the driveway. Create a foundation with paver base and leveling sand as required by code for a driveway.
WEST SIDE CINDER BLOCK WALL COATING. Add smooth surface or texturing to cinder block wall on west side of property. Coating shall smooth over all of surface on owner's side of cinder block wall, including the chips in last five feet (5') from street of the wall. Paint shall match the building stucco paint color.
PROTECTIVE STEEL POST. Install hollow cylindrical steel post at street end of cinder block wall on west side of property. Fill steel cylinder with cement. Post should descent at least two feet (2') in ground and ascend at least to height of cinder block at street end of wall. Consult owner for precise placement, dimensions, material and so forth.
VENTILATION AND EXHAUST STACK. Replace existing ventilation stack on right side of roof of main building with a new, corrosion-resistant stack.
MAIL BOXES. Install two mailboxes in locations specified by owner. Owner purchases mailboxes.
RIGHT TO PASS PLAQUES. Embed two brass plaques, inscribed with legal notice warning of unauthorized trespass, at sidewalk level in front of property. Embed one plaque in front of the main entry door. Embed the second plaque in front of the driveway gates. Owner will dictate the wording on the plaques.
# GARAGE INTERIOR
Do the following work in the garage.
ELECTRICAL. Do the following electrical work in the garage interior.
Electrical wall plates. Install three (3) new 2-socket GFCI electrical wall plates equally spaced along interior of east wall (shared with laundry room) at “base board level”.
Install three (3) new 2-socket GFCI electrical wall plates equally spaced along interior of east wall (shared with laundry room) at “counter top level”. Consult with owner for precise locations.
Install three (3) new 2-socket GFCI electrical wall plates along interior west wall.
Automatic garage door electrical supply. Install one (1) 2-socket electrical wall plate on ceiling near center to provide power for automatic garage door opener. Install circuit to supply electricity.
Fluorescent lighting fixtures. Install four (4) low-profile, four foot (4') long, dual lamp (2 tubes in each fixture), dual-pin electronic ballast, T8, 0-degree Fahrenheit starting temperature fluorescent light fixtures on garage ceiling. Each of the two pairs will be centered along width and depth dimensions of their respective half of the garage. Wire power for lighting fixtures in roof.
Garage door manual control switch. Install a manual garage door control switch either inside the laundry room on west wall shared with garage or on stucco between garage and laundry. Consult with owner for best solution.
Garage cabinets and shelves. Reinforce shelves in the built-in lockers at the back of the garage that span the full width of the back wall (north wall) of the garage. Install 2”x4” beams vertically beneath existing shelves to strengthen the load bearing capacity of the shelves.
WALLS AND CEILING. Do the following work.
Repair all interior dry wall on all walls and ceiling. Replace damaged dry wall surfaces if they can't be repaired.
Sand, prime and add two (2) coats of paint to all interior surfaces, including the walls, ceiling and the built-in cabinets and cabinet doors at the back of garage. Sand, prime and paint garage door jambs (1” x 7” beams) with two (2) coats of high-quality exterior latex paint . Jambs should be reconditioned to be in excellent condition.
INTERIOR PAINT SPECIFICATION. All painting shall consist of sanding existing surfaces, using a primer coat and two (2) coats of latex paint.
All ceilings: Behr “White” (1852), flat finish.
All walls: Behr “White” (1852), flat finish.
Base boards: Behr “Swiss Coffee” (1812), semi-gloss finish.
# LAUNDRY ROOM INTERIOR
ELECTRICAL. Do the following electrical work.
Electrical circuit wiring. Rewire electrical circuits in wall shared by laundry room and shop to accommodate relocation of washing machine and dryer. The dryer shall be closest to the laundry room door. The washing machine shall be be closest to the back of the laundry room.
Ensure electrical circuits can accommodate the maximum voltage and current load required for the washing machine and dryer.
Electrical sockets. Relocate electrical sockets for washer and dryer on the wall shared by laundry room and shop as necessary to accommodate the new positions of the washer and dryer. Install wall plates at the same height of the existing outlets. Ensure sockets accommodate owner's specific model washing machine and dryer electrical plug requirements.
Electrical wall plates. Install two (2) two (2)-socket GFCI electrical wall plates on the west wall of the laundry room, the wall shared with the garage, above the base board.
Install one (1) two (2)-socket electrical wall plate on the back wall above the base board.
LIGHTING. Install three (3) six-inch (6”)-diameter recessed lights on ceiling, 12V cans with standard threaded sockets, equally spaced from front-to-back, centered along long dimension of room (horizontally between walls shared with garage and shop). Install new light switch.
GAS AND WATER PLUMBING. Inside wall between shop and laundry, redo the gas and water and gas plumbing as necessary to relocate washer and dryer.
Water heater. Add a platform for the water heater.
Utility sink plumbing. Install new plumbing (exterior to wall) for sink. Install new Moen single handle faucet. Customer makes selection.
Washing machine and dryer installation. Install washer, dryer and accessories such as electrical chords, plugs, etc. Customer purchases appliances.
WALLS AND CEILING. Lightly sand and smooth all surfaces. Add two (2) coats of paint to entire laundry room. Ensure a uniform, quality finish.
Cover water heater and sink while sanding, prepping and painting; or remove from laundry room to a safe location to prevent damage during construction. Cover floor with rosin paper before beginning work.
Cover washing machine return pipe (drain pipe). No debris should be allowed to fall down drain pipes. Remove all paint, plaster or other residue from all plumbing pipes, stop valves, handles, water heater, etc. Clean area near stop valves. It should be as clean as when purchased from store.
INTERIOR PAINT SPECIFICATION. All painting shall consist of sanding existing surfaces, using a primer coat and two (2) coats of latex paint.
All ceilings: Behr “White” (1852), flat finish.
All walls: Behr “Cozy Cottage” (740C-2), flat finish.
Base boards: Behr “Swiss Coffee” (1812), semi-gloss finish.
UTILITY VANITY. Sand metal vanity to remove all rust. Prime and add two (2) coats of paint. See section Interior Paint Specification for details. Protect basin surface during this work.
ENTRY AND DOOR. Install a new, solid core, paintable, fiberglass door, with the same half fan-light window glass design used in the shop door and main building front doors. Install a high-quality handle for exterior use. Door will have a bronze kick plate.
Paint the door the same color as the building exterior.
Reframe laundry room door so it has the same height as the shop door. Build new jambs and casings. Consult with customer regarding selection.
Window. Clean window area thoroughly.
Electrical wiring for low-voltage security system. Run security system signal supply wiring into garage. One candidate solution is to bring cable conduit under patio cement from north-west corner of main building. Conduit shall come up near wall to left of laundry room door. Conduit can punch through garage wall and into east side garage wall (the wall shared with the laundry room).
Please see paragraph entitled “Electrical wiring for low-voltage security system” in section entitled Main building exterior. Consult with owner for best and least disruptive/destructive solution.
# SHOP INTERIOR
The “shop” is the fifteen foot square (15' x 15') room adjacent to the laundry room. The following work needs to be done.
ELECTRICAL. Do the following electrical work.
Electrical wall plates. Install five (5) two-socket electrical wall plates in interior of shop as follows:
Two (2) two (2)-socket GFCI wall plates on the west wall at the base board level.
Two (2) two (2)-socket GFCI wall plates on the west wall at the counter top level, above the counter top (see below or counter top specification). Consult owner for precise locations.
One (1) two (2)-socket wall plate on each of the north, east and south walls. These wall plates shall be at the base board level.
Electrical conduit demolition. Remove all electrical conduit visible in interior of room and place inside walls as necessary to supply electrical outlets. Upgrade electrical sockets to GFCI, eight (8), 2-socket wall plates total near base molding. Install three (3) two-socket electrical outlet plates above counter top on wall adjacent to laundry.
Interior lighting. Install up to four (4), six-inch (6”)-diameter recessed lights, 12V cans with standard threaded sockets in the ceiling of the same brand, model and style as those in the main building living rooms. Fixtures should accommodate dimmable compact fluorescent, LED or incandescent flood lights like those in the main building. Consult owner for layout of recessed light cans.

Install two (2) dimmer switches to control two (2) banks of recessed lights per owner's or interior decorator's design. That is, the four (4) recessed lights shall be configured into two (2) banks of two (2) lights each. Owner specifies grouping, layout and configuration.
ENTRY DOOR.
Install a new fiberglass door, with half fan-light glass, door hardware; material, style, etc. to be determined. Door will have a bronze kick plate. Consult with owner.
Paint the door the same color as the building exterior.
Front door threshold. Build some kind of threshold at the base of the shop door that will stop water from entering the shop. The solution shall ensure that the bottom of the door is not affected by water. The solution must provide an adequate barrier that stops the entry of any water into the shop or any water damage to the door. Consult with owner for the best solution.
WALLS AND CEILING. Install new interior dry wall on all walls and ceiling. Prime and put two coats of paint.
INSULATION. Install new insulation in ceiling and in all walls. Use R-19 insulation for walls and R-30 insulation for ceiling.
COUNTER TOP ASSEMBLY. Install new standard depth and height quartz counter tops along the one wall shared with laundry room. Brand and model to be selected by interior decorator. Consult owner for details of extend of counter top, dimensions, and so forth.
Sink. Install a new double stainless steel sink in counter top with approximate dimensions 32” W x 18” D. Consult with owner regarding details.
Plumbing fixtures. Install a single-handle faucet in sink.
Cabinetry. Install new standard-height cabinets below counter top. Cabinets and counter top shall be selected by interior designer. Leave room beneath counter top for a half-height refrigerator.
SHOP FLOORING. Install Eternity Floors, Sapphire line, Red Ancient Pine, model VG1052, 12mm thick laminate wood flooring like that in main units.
INTERIOR PAINT SPECIFICATION. All painting shall consist of sanding existing surfaces, using a primer coat and two (2) coats of latex paint.
All ceilings: Behr “White” (1852), flat finish.
All walls: Behr “Cozy Cottage” (740C-2), flat finish.
Base boards: Behr “Swiss Coffee” (1812), semi-gloss finish.
MISCELLANEOUS. Install almond color, glossy finish light switch plates.
# BACK STRUCTURE EXTERIOR (GARAGE, LAUNDRY & SHOP)
Do the following exterior work on the back structure.
SHOP STRUCTURAL REPAIRS. Do the following structural repairs.
Shop north wall. Repair or completely replace the north wall damaged by the tree previously located on the neighbor's property to the north.
Shop roof. Fix the flat roof as necessary. Reinforce the roof as necessary with one inch (1”) plywood. Add new exterior roofing as necessary. This work needs to be assessed. Ensure roof slopes downward towards patio to ensure water will run towards rain gutters.
Shop windows. Install two (2) new Certainteed brand double-paned, low-E windows to replace existing windows. Dimensions of both windows are 58” W x 36” H.
ELECTRICAL PANEL.
Install new weather-proof electrical sub-panel on outside of east wall. Conduit carrying wiring from main panel is already in place.
EXTERIOR ELECTRICAL WALL PLATES.
Install one (1) two-socket, corrosion-resistant weather-proof outdoor electrical socket, like those on main building exterior, near the top-center of the east wall of the shop. Install a new security light with motion sensor near the top of the east wall.
Install one (1) two-socket (2-socket), corrosion-resistant weather-proof outdoor electrical socket, like those on main building exterior, near the bottom-center of the exterior east wall of the shop.
Install one (1) two-socket (2-socket), corrosion-resistant weather-proof outdoor electrical socket, like those on main building exterior, near the bottom-center of the exterior south wall of the back structure, centered between the laundry and shop doors.
EXTERIOR LIGHTING. Add the following exterior lighting to the back structure.
Garage security light. Install new security light with motion sensor above garage door. Electrical supply and fixture are already present.
Laundry room door light. Wire and install a wall-mounted electrical lighting fixture for the laundry room entrance. The fixture shall be to the left side of the laundry room door on the short segment of wall delineating the garage from the laundry room. The fixture shall be located at the same height as the shop exterior light fixture. Customer purchases lighting fixture.
Shop entry door light. Move existing electrical wall plate upwards by amount specified by owner. Install exterior lighting fixture. Customer purchases lighting fixture.
STUCCO REPAIR AND EXTERIOR PAINT. Do the following work on the back structure building exterior surface.
Power wash or sand all eaves and fascia boards. Prep, prime and add two (2) coats of paint to fascia boards and stucco.
Redo stucco (scratch coat, brown coat, color coat) around windows that will be replaced.
Repair/replace all damaged stucco around detached structure (garage, laundry and shop).
Paint entire building stucco with two (2) coats of paint to match existing color coat of main building (MERLEX brand “cafe mocha”) per customer's approval. Final product shall exhibit uniform color and visual texture everywhere.
Wait a minimum of three (3) days between applications of stucco coats or paint coats to allow time for thorough drying.
CINDER BLOCK WALL AT PROPERTY NORTH BORDER. Build wall to height of eight feet (8') (height of actual cinder block wall, without lattice) as measured from the neighboring property ground level, which is higher than the ground level of owner's property. Add rebar in cinder block columns where no rebar exists currently. These holes (columns) exist between the existing rebar.
Resurface cinder block with smooth texture cover; final selection of material shall be made by owner upon consultation with contractor. Paint shall match the building stucco paint color.
Note: contractor shall verify whether a special permit or dispensation is needed to build the wall to eight feet (8') height measured from the north side (neighboring property's side) ground level.
# GENERAL BACK STRUCTURE SPECIFICATIONS
This section describes work that falls under both interior and exterior work for the back structure.
PATIO AND GARDEN SLATE. Install 10mm thick multi-color slate in the patio and back garden. The slate surface shall cover all of the patio cement from the driveway paving stones to the redwood fence, stopping at the breezeway cement. The slate shall also cover the entire back garden, except for an approximate two-foot (2') dirt track between the slate and the back cinder block wall. Build a winding edge between the slate and the dirt adjacent to the back wall. Consult with owner on design details. Consult with owner on how to slope surface for drainage. Ensure slope drains water away from the laundry and shop.
Customer selects slate.
SATELLITE TV, CABLE TV, CLOSED-CIRCUIT TV (CCTV), INTERNET AND TELEPHONE CONFIGURATION AND WIRING. Install all A/V, telephone and Internet wiring for the garage and shop as follows. All wiring should be in flex conduit.
Shop satellite TV signal supply wiring. Install one (1) exterior wall plate with one (1) coax connector on the inside of the parapet of the garage west wall to supply a satellite TV connection point for the shop. The coax will run in the ceiling joist space to the shop and down the shop walls to the specified location of the shop's A/V wall plates.
Shop telephone signal supply wiring. Run the fifth telephone supply pair from the phone box, under the breezeway cement, in the dirt along the redwood fence, underground in the patio between the patio cement and garden and up the east wall of the shop to the interior wall plate locations. Use shielded, twister pair phone line in conduit.
Shop Internet signal supply wiring. Run Cat 6A compliant cable in conduit for the Internet signal supply wiring from the east side of the main house, under the breezeway cement, in the dirt near the redwood fence, under the stone in the back garden and up the east side of the shop wall to the interior wall plate locations.
Shop interior Internet and telephone wall plate configuration. Install one wall plate on the east wall of the shop interior, horizontally centered under the east window at the base board level with the following connectors: one (1) F-type connector for satellite or cable TV service, one (1) RJ-14C/RJ-14W phone jack, one (1) RJ-45S Cat 6A compliant jack for Internet connection.
Garage Internet signal supply wiring. Run RG6Q (RG6 Quad) cable in conduit for the garage Internet connection from the east side building cable supply to the garage. Run the cable under the breezeway cement, along the dirt strip adjacent to the redwood fence, under the garden adjacent to the patio cement, up the east side shop wall and into the ceiling joist space of the back structure all the way to the garage and down the garage east wall to provide signal supply for a single wall plate at the base board level. Location shall be specified by owner. Install wall plate with one (1) RJ-45S Cat 6A compliant jack and connect wiring.
Garage closed-circuit TV (CCTV) signal supply wiring. Run Siamese RG59 cable (containing signal and power) from all security camera locations to the garage. From the main building, run the cable under the patio cement near the border at the patio cement and the garage stones and up the wall between the garage and laundry room and finally into the garage. Owner shall specify final location of wires in the garage.
Garage interior wall plate configuration. Install one wall plate on the east wall of the garage interior at the base board level. The wall plate shall have one RJ-45S Cat 6A compliant jack connected to CAT 6A cabling as specified in this section.
# MEASUREMENTS
This section contains measurements for engineered wood flooring, floor and and wall tile, and slate flooring. All numbers are in square feet. Measurements include both apartments, laundry and shop.
ENGINEERED WOOD COVERED FLOOR AREA MEASUREMENTS.
Downstairs (excluding kitchen)	770
Apartment 1 large bedroom floor (including closets)	262
Apartment 2 large bedroom floor area (including closets)	182
Small bedrooms floor area (including closet)	364
Upstairs hallways	20
Shop floor	225

TILED FLOOR AND TILED WALL AREA MEASUREMENTS.
Kitchen floor area	100
Kitchen wall tile area	64
Downstairs bathrooms floor tile	32
Downstairs bathrooms wall tile	112
Upstairs bathrooms floor tile	70
Upstairs bathrooms wall tile	140

QUARTZ COUNTER TOP MEASUREMENTS.
Kitchen counter top quartz	36
Upstairs vanity top quartz	16

SLATE TILE AREA MEASUREMENTS.
Patio cement area to be covered with slate (excluding breezeway)	210
Garden area to be covered with slate	255

MISCELLANEOUS MEASUREMENTS.
Front pavers between sidewalk and curb, sq. ft.	72
Cinder block wall area (both walls), sq. ft.	348
Redwood fence, linear ft.	60
Base board length for apartment 1 & 2 interior, linear ft. (actual linear ft. = 493)	500

# MISCELLANEOUS
DRY WALL. No dry wall product shall be made in China.
HOSE BIBS ON EXTERIOR SPIGOTS. Ensure that there are no leaks from hose bibs when a hose in good condition is attached. Install new brass threaded spouts on any leaking exterior hose bibs. If leaks can be fixed with a simpler solution such as winding hose bib with teflon tape, use the simpler solution.
POSTAL LOCK BOX. The postal service will install a postal lock box near the front wrought iron door.
WINDOW CAULKING. Caulk the full exterior perimeter of all windows. Ensure there are no leaks in any of the windows.
ELECTRICAL CIRCUIT CONFIGURATION. For each of apartment 1, apartment 2, garage, shop and laundry, put lights and electrical receptacles/sockets on separate circuits.
# PRE-CONSTRUCTION RESOLUTION TOPICS
This section lists points that need resolution or consultation. I would like to discuss and resolve these issues before we finalize the contract, perhaps during our pre-construction meetings.
Cinder block walls. Height of wall near shop. I want 8' as measured from neighboring property's side. What material to smooth coat it? Stucco?
Height of driveway pavers and patio slate. The patio slate will be higher than the driveway pavers. What can we do about that?
Satellite TV antenna support. Discuss best solution for additional fascia board on east side of building to support satellite TV dish installation. The goal is to avoid damage to building yet accommodate satellite service that tenants might want.
Main entrance wrought iron door. Do I need for a thicker gauge main entry wrought iron door?
Bathroom vanities and sinks. Are the sinks too large for the vanities?
# ALLOWANCES

Allowances are defined as estimated costs of materials, appliances, and equipment that have not yet been specifically identified, such as tile, wallpaper, and light fixtures. Owner will make the necessary selections promptly so as to prevent the progress of the work from being delayed. / The only allowance items are those identified by Owner herein. As to these allowance items, the only allowance is for the cost of the material involved and labor to install the item must be included and contemplated by the Contract Price. Any change in the material covered by an allowance shall result in either an additive or deductive change order for the exact cost of the actual material purchased and consumed in the Work. No increase in the Contract Price shall be provided to Contractor for claims that any particular material was more costly or time consuming to install than contemplated by Contractor. / The items and allowances are contemplated herein: / Front Doors $1,000 / Front Door Hardware $300 / Front Door jambs, frames, casings, thresholds $300 / Laundry Room Door $100 / Shop Door $100 / Recessed Light Trim ($58 each) / Garage Door, Casings, Remote Control, Hard-Wired Control, Sensors $1,000 / Apartment 1 downstairs built-in bathroom nook cabinet $400 / Apartment 2 downstairs built-in book shelf. $400

OWNER / VARTAN PIROUMIAN / __________________________________ / (Signature) / __________________________________ / (Date)	CONTRACTOR / __________________________________ / (Contractor’s Name) / __________________________________ / (Signature) / Contractor’s Performance Guaranteed Personally: / __________________________________ / (Officer’s Name) / __________________________________ / (Signature) / __________________________________ / (Date)