Dear Customer,
congratulations on the purchase of the EMP-Centauri product. Before its installation and putting into operation, read carefully the entire operation manual. Keep the purchase and rework (if any) records for future need.
# 1) Field of Application, Warranty
The products are designed for the optical distribution of satellite and terrestrial TV and radio signals. Fiber optic link is an advantageous supplement to traditional coaxial cables either in extensive distribution networks (with distances more than 100 metres) or in the cases where several coaxial systems should be feeded from remote common antenna.
EMP-Centauri's PROFI CLASS products are covered under 4 (four) years warranty from the date of purchase. The warranty shall not apply to the product used for other than the specified purpose. The user will be responsible for injury or material damage which may arise in consequence of any product use in contradiction with the manual. Repairs or any interventions in the product may be performed only by EMP-Centauri company, or other companies authorized by EMP-Centauri.
# 2) Technical Specifications
OT1/1+1PUU-2 is a converter of satellite & terrestrial TV and radio HF electrical signals to transmission via the fiber optic (optical transmitter). A through coaxial output is available for the parallel coaxial distribution. Power supply is expected either from the coaxial output or DC socket.
OR1/1PCA-1 is a back-converter of fiber optic transmission to electrical HF signals (optical receiver). It is powered from the output coaxial cable.
SPECIFICATIONS	OT1/1+1PUU-2	OR1/1PCA-1
Number of Inputs	1 coaxial	1 optical
Number of Outputs	1 coaxial, 1 optical	1 coaxial
Frequency Range	88–2150 MHz	88–2150 MHz
Insertion Loss (avg)	0 dB
Minimum Input Level	70 dBuV
Maximum Input Level*	90 dBuV
Current Consumption (avg)	150 mA (12 V)	35 mA (12 V)
DC current pass	400 mA
Light Wavelength	1310 nm	850–1600 nm
Optical power	5 dBm
Maximum Input Optical power		2 dBm
Connectors	F (coaxial), FC/PC (optical)	F (coax.), FC (optical)
Dimensions (w,d,h)	10.7 x 5.9 x 3.2 cm	7.0 x 6.0 x 3.2 cm
Temperature Range	–30 °C – +60 °C	–30 °C – +60 °C

* TERR: EN 50083-3/60dB IMA3 [dBuV]; SAT: EN 50083-3/35dB IMA3 [dBuV]
# 3) Product Takeover
Make sure that the product is not damaged. Please contact your dealer in the case of damage.
# 4) Product Storing and Installation
We recommend the device to be installed and serviced by the qualified technician.

The product must not be stored and installed
- in the place with excessive humidity
- in the place with excessive dust pollution, mechanical vibrations or impacts
- in the place out of temperature limits specified in the section 2 Technical Specifications
- close to heat sources (radiators or air ventilators, direct sunshine etc.)
- in the reach of children.
Do not expose the apparatus to dripping or splashing. Use the apparatus only in moderate climates (not in tropical climate).
Fix the product firmly on a wall or another hard and inflammable surface with screws and dowels.
- The product shall be in no case held only by the connected cables.
- Do not cover the product (with curtains etc.).
- Do not place any containers with liquids (vases, glasses etc.) or naked flame sources (lighted candle etc.) on the product or near the product.
# 5) Product Connection
Connect the product in accordance with this manual and valid regulation in your country. Use high quality 75 Ω coaxial cable designed for satellite reception. The coaxial cables shall not be broken, the minimum bending radius should be 5 cm. Mount the F connectors (screw, crimp or compress type) on the ends of coaxial cables. Connect the F connectors into the F sockets of product and fasten them with an appropriate force.
For optical link use only single mode “SM” fiber cable terminated with FC/PC (FC/APC*) connectors. The fiber cable can be bended according to specifications of the cable's manufacturer. When connecting the cable to the product take off the protective caps from both connector and receptacle and insert carefully the ferrule into the hollow in proper mutual orientation (as indicated by the key on the metal body of the connector). Fasten the connector by screwing to the receptacle.

OT1/1+1PUU-2:
- Connect F socket marked “COAX IN” by coaxial cable to the output of the LNB or other distribution unit with current consumption up to 400 mA.
- Connect F socket marked “COAX OUT” by coaxial cable to the input of multiswitch or other distribution unit. It is required to use terminator 75 Ohm if the coaxial output is not in use.
- Connect FC/PC receptacle marked „FIBER OUT“ by fiber cable terminated by FC/PC plug to the input of optical receiver, splitter or other optical equipment.
- External power supply (e.g. PA12) must be connected to the socket marked „12V DC IN“ if the device is not powered from output coaxial cable.
OR1/1PCA-1:
- Connect FC receptacle marked „FIBER IN“ by fiber cable terminated by FC/PC or FC/APC* plug to the output of optical transmitter, splitter or other optical equipment.
- Connect F socket marked „COAX OUT“ by coaxial cable to the input of multiswitch or other distribution unit.
*The signal/noise ratio can be improved using FC/APC connector at the input of the receiver OR1/1PCA-1.

Note: The optical splitter for up to 16 outputs can be placed between OT1/1+1PUU-2 a OR1/1PCA-1.
It is necessary to insert optical attenuator 3 dB if there is direct link (no splitter) between OT1/1+1PUU-2 and OR1/1PCA-1.
The wiring examples are shown in the section 10) Wiring Diagrams or at www.emp-centauri.eu.
# 6) Product Settings
There are no special settings for these products.
# 7) Safety
Due to security reasons the product and wiring in which the product is connected, must be grounded properly. Make sure the antennas are grounded properly. Connect all devices to power grid only after all connections are finished and checked. Never work on the wiring (including satellite and terrestrial receivers, TVs) during or before a storm. A lightning stroke into the antenna may cause dangerous overvoltage in the product metallic parts. The product should be disconnected from the wiring immediately if it gets into contact with liquids (dropping water, spilled drinks etc.).
# 8) Product Maintenance
Always disconnect the product from wiring before performing any maintenance of the product. If you have to enter places with a risk of fall, pay attention to your safety.
By the maintenance it is basically meant the cleaning of the product. Use only dry cloth to clean the product and do not use any liquid agents. Coaxial cables installed outdoors should be replaced once in a few years. Unscrew all F connectors and clean connector contacts, resp. shorten the coaxial cable by approx. 2 cm, every 2 years.
# 9) Symbols Explanation
certificate of conformity
According to EU directive, electric and electronic devices which are identified by one of the following symbols must not be disposed of together with municipal waste. When disposing of the old device, use local waste collection and separation systems.

# 10) Wiring Diagrams

Instruction Manual		1/003706 A
OT1/1+1PUU-2 / OR1/1PCA-1

# 11) Contakt
EMP-Centauri s.r.o. / 5. kvetna 690 / 339 01 Klatovy 4 / Czech Republic	tel: (+420) 376 314 852 / fax: (+420) 376 323 809 / info@emp-centauri.cz / www.emp-centauri.eu

návod k použití	1/003706 (OT1 OR1 EN)		stav změny : A
datum : 5.12.2013	vypracoval : P. Hajčiar	přezkoušel :	schválil : M. Váňa
	podpis :	podpis :	podpis :

1 of 4
3 of 4
2 of 4
4 of 4