Sensor Multiplexor
Providing additional sensors for the Handy Board
Author:	Doug Rinckes (doug.rinckes@iname.com)
Date:	January 2001
# Introduction
This project was prompted by a need to run a number of current hungry sensors off a Handy Board.
This solution allows a large number (32) of sensors to be connected, using just two analogue or digital in ports, and two digital out ports.
Only the sensor being sampled (and its counterpart) is powered - all others have their ground connection disabled. This helps to preserve power, especially where infra-red reflectance sensors are used.
# Circuit Diagram

The 74HC93 provides two four bit counters. The counter and reset lines are tied together, so they count in step.
The output lines from each counter are fed into a 4 to 16 line decoder chip (MC14514). Although these chips have a latch, to store the value if the input lines change, we won't be using it.
The decoder sets one (and only one) of the output lines high depending on the input value. This triggers a transistor which grounds the sensor.
# Stripboard Layout