Application Note

5x80
Power modes

by Dieter Fauth

Last revision of this document: 2007-01-10

# Overview
This application note describes the power requirements of the 5x80 devices in various situations. It shall help you to optimize battery life and minimize current consumption.
## Required knowledge
This document is written for engineers.
## Revision History
2006.12.13	First release

## Normative References
This Document incorporates, by dated or undated references, provisions from other publications. These normative references are cited at appropriate places in the text and the publications are listed hereafter. For dated references, subsequent amendments to, or revisions of, any of these publications apply to this Standard only when incorporated in it by amendment or revision. For undated references the latest edition of the publication referred to applies.
ISO/IEC 646	(also known as the ASCII std.)
ISO 10646	(also known as Unicode)
Universal Serial Bus Specification, Revision 2.0, April 27, 2000
## Abbreviations
For the purposes of this Document, the following abbreviations shall apply:
Byte	An ordered sequence of eight bits considered as a unit.
DEC	Decimal value
HEX	Hexadecimal value
MSB	Most significant byte
LSB	Least significant byte
RX	Receiver
TX	Transmitter
## Notations
Within each byte the most significant bit is bit 7 and the least significant is bit 0. Accordingly, the weight allocated to each bit is:

Bit value	bit 7	bit 6	bit 5	bit 4	bit 3	bit 2	bit 1	bit 0
Weight	128	64	32	16	8	4	2	1

Multiple byte values are always used in the so called "little endian" format. That means the LSB is stored in the lower address.
2 Byte values:
Address	0	1
Weight	LSB	MSB
Example 0x1234	0x34	0x12

3 Byte values:
Address	0	1	2
Weight	LSB		MSB
Example 0x123456	0x56	0x34	0x12

4 Byte values:
Address	0	1	2	3
Weight	LSB			MSB
Example 0x12345678	0x78	0x56	0x34	0x12

Decimal numbers are written without any further attribute.
Hexadecimal numbers are written in the notation of the language C++.
Examples:
HEX:	0x10
DEC:	16

# Power states
The device has several power modes. In each mode it needs a different amount of power. For example it needs more power to scan a barcode than to simply communicate with a host system. The reasons are the illumination and the aimer that take a substantial amount of power.
If there is no host communication and no scanning, we can further reduce the power by slowing some clocks down.
Said that, here are the power modes (all current values are for 5V. For 3.3V operation, they are higher):
- Power off
  The device has no power at all, so there is no power consumption.
  After applying voltage to the device, it takes about 1.5 seconds until it is under full operation.
- Powerdown
  Device has turned off power to all circuits except the ones required to wake up.
  Current consumption is about 500 µA.
  Startup time to full operation is about 1.5 Seconds.
- Stop
  Device has slowed down or turned off certain clocks and unused circuits.
  Current consumption is about 3 mA (10 mA max).
  Startup time to full operation is about 300 µSeconds.
- Idle
  Device is ready to communicate but does not scan.
  Current consumption is about 25 mA..
- Scanning
  Device is under full operation, Imager is active, Illumination is on, ...
  Current consumption is about 250 mA .. 400 mA depending on aimer type and mode.

Events and timeouts do control in which of the above power mode the device operates. The device slows down its operation to save power after some time of working in Idle mode. There is no direct way or command to enter a lower power state. You can configure the timeouts and behavior to fit your requirements.

Time
Power
Scanning
Idle
Stop
Stop
Events and timeouts:
- nTrigger input
- nWake input
- Communication requests
- Communication timeout
- Trigger timeout

The figure to the right illustrates the relative power requirements in some modes.

Find more details in the example section.
## Wakeup events
Here we describe the events that boost the power mode into a higher power state.
### Wakeup from Stop mode
In Stop mode the device does wake up in about 300 µSeconds by these events:
- nTrigger input is activated
- CTS input changes its state
- Serial data byte is received (byte will be lost)

Waking up takes about 300 µSeconds, in this time you could send several characters with 115KBit/Sec, but the Imager is not ready to receive it yet. So please take this time into account before sending commands.
### Wakeup from Powerdown mode
In Powerdown mode the device does wake up in about 1.5 Seconds by these events:
- nTrigger input is activated
- nWake input is activated
### Wakeup from Power off mode
This is trivial, any power applied to the Vin pin will bring the device into its normal (Idle) operation.
## Sleep events
Two sleep events control the decline of the power modes towards less power.
### Communication timeout
This timeout can be used to bring the device from Idle to Stop mode. It is applicable to the RS-232 communication and will be ignored with all USB interfaces.
The timeout will be reset by all events that boost the power mode into a higher power state. Especially any communication request from the host does reset the timeout. After it expires, the device gos into Stop mode.
### Trigger timeout
This timeout can be used to bring the device from Idle or Stop to Powerdown mode. It is applicable to the low power trigger mode only.
The timeout will be reset by all events that boost the power mode into a higher power state. After it expires, the device gos into Powerdown mode.

## State diagrams
The power states depends on the settings for the interface and the trigger.
### Low Power trigger
This diagram is valid for the low power trigger mode for the RS232 interface (TRGMOD2).

### Manual / Software Trigger
This diagram is valid for the normal trigger mode for the RS232 interface (TRGMOD0). There is no Suspend state.

### USB
The USB does control the power states from the host system. There is no Stop state because the USB needs the clocks running all the time. The nTrigger and nWake inputs can wakeup the host system via the “Remote Wakeup” mechanism of the USB.

# Commands
This section describes the commands required for controlling the power modes. Please find more details about commands in the users guide. Here we want to concentrate on the power modes, so we keep the examples simple.
## Communication timeout
This timeout can be used to bring the device from Idle to Stop mode. It is applicable to the RS-232 communication and will be ignored with all USB interfaces.
The timeout will be reset by all events that boost the power mode into a higher power state. After it expires, the device gos into Stop mode.
The command is (in C notation)
\x16m\r232LPT#.
With # = number of seconds, default is 0, the allowed range is from 0 to 300. 0 means this feature is turned off (never goes to Stop mode).
Example: Timeout is 7 seconds:
\x16m\r232LPT7.
## Trigger timeout
This timeout can be used to bring the device from Idle or Stop to Powerdown mode. It is applicable to the low power trigger mode only.
The timeout will be reset by all events that boost the power mode into a higher power state. After it expires, the device goes into Powerdown mode.
The command is (in C notation)
\x16m\rTRGLPT#.
With # = number of seconds, default is 120, the allowed range is from 0 to 300.
Example: Timeout is 20 seconds:
\x16m\rTRGLPT20.
## Low power trigger
Since the restart time out of the Powerdown mode is about 1.5 Seconds, there is a separate command to allow the device to enter this mode. It is part of the trigger commands.
\x16m\rTRGMOD2.
If you want to turn it of, then select the manual trigger mode (normal power).
\x16m\rTRGMOD0.
# Hardware considerations
Systems that partially power down require some care in its design. There are a few potential pitfalls that can prevent the lowest possible power consumption.
## Avoid back power via the RS232 lines
If the device is in its Powerdown mode, there could be a current flow from input lines to internal VCC (and then to GND). This current can discharge you batteries on the long run, so it is a good idea to avoid this kind of losses and ensure that these inputs are low.
Depending on the usage case we need to distinguish two cases.
### RS232 Inverted
This mode is used to connect to real RS232 ports. The RDX line is low (or negative) in its idle state, so we are done with this line. But the CTS input needs some care. If it is high it can cause the above problems, so please ensure it is low if the device goes into the Powerdown mode.
### RS232 non-Inverted
This mode is used to connect to UARTS directly. Here we need to take care for both the RXD and the CTS lines. Especially the RXD can make trouble if your UART does not allow to lower it. Perhaps there is a “Send Break” functionality, that lowers the line to low.
## Avoid open inputs
The RXD and the CTS inputs are not equipped with pull down resistors, so it is required to always connect them to GND[1] if they are not used.
[1] You could use the VCC as well, but that can cause other problems while the device is in its Powerdown mode.
FIXME: Add some clarification.

## Current measurement errors
As we learned above, the RS232 lines can feed a current into the device. If we now measure the current in the GND line, we might run into situations where the current via the clamp diodes is higher than the current we want to measure.
We can even see a negative current caused by a negative voltage connected to the RXD or CTS inputs.

So it is recommended to measure the current in the VCC line. Unfortunately this causes trouble with Oscilloscopes, their probes are usually grounded. As a solution you need a differential probe or some circuit with one of the modern high side current measurement chips.

# Examples
## RS-232 communication with moderate power
This is for moderate power savings requirements. The device stays in Stop mode for most of the time (3 mA). Only for scanning or communications there is a need for more power.
We do not want to use Powerdown mode due to the relative slow startup time in this example. So we choose a communication timeout of 5 Seconds. We can wake up the device with either a change on the CTS input or a throw away character on the Rx input. The nTrigger input works as well.
To setup we need to send these commands (in C notation):
\x16m\r232LPT5.
To be sure that other experiments to not influence us here we select the “manual or serial trigger mode”. It is the default behavior of the device.
\x16m\rTRGMOD0.
Or we can send both commands at once:
\x16m\rTRGMOD0;232LPT5.
We assume that the baudrate etc is already correct.

The figure below shows a scan directly started from Stop mode by the nTrigger input going active .

Time
Power
Scanning
Idle
Stop
Stop
5 Seconds timeout
Trigger event
Barcode is scanned

## RS-232 with strict power saving requirements
This is mainly for battery operated devices. The device goes into Powerdown mode for most of the time, so it does not draw too much current. Here we need to accept the startup time of almost 1.5 Seconds. Only the inputs nTrigger and nWake can wake us up.
To setup we need to send these commands (in C notation):
Communication timeout of 7 Seconds:
\x16m\r232LPT7.
Manual trigger with low power:
\x16m\rTRGMOD2.
Trigger timeout of 20 Seconds:
\x16m\rTRGLPT20.
Or we can send all commands at once:
\x16m\rTRGMOD2,LPT20;232LPT7.
We assume that the baudrate etc is already correct.

The figure below shows a scan directly started from Powerdown mode by the nTrigger input going active .

Time
Power
Scanning
Idle
Powerdown
Stop

Powerdown
Timeout can be configured with 232LPT command
Timeout can be configured with TRGLPT command

Cleanup

Trigger event

The SDK for the 5x80 does not support the Powerdown mode directly. There is no standard way of activating the required inputs.
## USB with moderate power
With the USB interface we can not reach the low power modes we can use for the RS-232 interface. The main reason is that the USB controller and its clock needs to run all the time. We cannot turn it off like we do with the RS-232 controller. Only if the host does set us into the USB suspend mode, then we can go into low power modes. So there is nothing to setup here, everything works with the default values.

Time
Power
Scanning
Idle
Idle
Trigger event

# FAQ
Every time the Imager will ignore the very first command I send.
Your Imager is probaly in Stop mode when you try to communicate with it. In this mode it wakes up by a received byte, but that byte is lost. See page 6 for more details
Why does the SDK not support the Powerdown mode?
Power Down’ mode cannot be used with the current HHP SDK. Waking up from Powerdown mode requires hardware input on lines other than the typical RS-232 standard serial interface (TX/RX RTS/CTS). With some additional hardware (a transistor) you can use the RTS output of the host to activate the nWake or nTrigger lines.
FIXME
Why is the wakeup byte lost?
The serial controller (UART)has no clock at this time, so it cannot receive and store the byte. Only the change in the signal does cause the wake up event.
Can I hold the nWake input always active to prevent the device from entering the Powerdown mode?
Yes, that works. Though it is not recommended. It is better to treat that input as if it would be edge triggered.
Are there alternate tools to the SDK for getting started with the 5x80?
Yes, there are the official tools QuickView, VisualMenu and VisualExpress. There is also an in-official collection of source code examples for C++/MFC, it is called AdaptusESC (Example Source Code).