## Constant
-	com.ergotech.vib.manipulators.Constant

Description
This manipulator is used to store a constant parameter (Variable) that is sent as a Value Object to its listeners as the logic in the application is being started (“fired early”). This data source is fired exactly one time.

The Constant is usually used to initialize a property of a component or to initialize an input value. The Value Object type can be specified, as well as an initial Color and Quality.
Inputs
Input: No input
Outputs
Output: The output is the constant value set in the properties
Properties
This has the properties of a Data Source plus

- Constant Value: The data value of the Value Object. This defaults to 0.
- Type: Select the data type for the Value Object. This defaults to Long Value Object.
- Fire Late ?: This defaults to False which means the Constant Value Object will be sent as early as possible in the initialization of the logic. If this is set to True then the Value Object is sent to the target after all the components have been initialized. This is equivalent to using a Startup Trigger .
- Initial Quality: Select the Quality of the Value Object. This defaults to Good Quality.
- Value Color: if you want to set an initial Color of the generated Value Object, then set this to a non-null Color value. Be sure that Send Color is set to True.
- Send Color: This defaults to True so that the Color set in Value Color is added to the Value Object sent when this component fires.
- Timebase (Expert): You can set a timebase in seconds (this defaults to 0.0 for no timebase). If you set a timebase the Constant Value will be fired every timebase tick.

Note:

The Constant has a timebase, however the use of the timebase is discouraged. The purpose of a constant is a one-time initialization of a system. This will occur only once, when the screen loads in MIStudio or in MIX. While the behavior is MIStudio is accurate, it has been confusing to some users who expect the constant to send values more frequently. The timebase allows the Constant to assume that behavior, but the logic will be triggered whenever the constant fires which is probably not desirable or useful if the value is constant. For triggering events, such as saving information to a database using the Triggered Historical component, the Extreme Server or the Synchronized Clock Tick is preferable. The timebase can be useful for debugging, but should generally be returned to zero before deployment.

When using the Constant (or Startup Trigger) in MIStudio, the Constant Value will only be sent one time, when the screen is first loaded. For debugging purposes you can set the Constant Value to a different value to force the sending of the Constant Value again.

See Also:
Startup Trigger is used to trigger a component with a Value Object after the logic is initialized (“fired late”).