The Superposition Theorem
Defining an unknown quantity by adding up the individual contributions to that unknown.

Most usually, the unknown quantity is a voltage that can be found by adding the individual contributions to that voltage, because the corresponding currents are additive.

Example 1: Find the voltage across VO in the following circuit.
Using the superposition theorem, V sub O = V sub O1 + V sub O2 . Split the circuit into two separate circuits in which each one has only one voltage source.
V sub O1 = Using the voltage divider equation, abs{V sub O1} = {E sub S1 cdot R sub 2} over {R sub 1 R sub 2} = {10v cdot 20K%OMEGA} over { 25K%OMEGA} = 8v then determine the polarity by observing the polarity of the first source: V sub O1 = +8v

Then isolate ES2 and solve for the voltage of R1 again:

abs{V sub O2} = {E sub S2 cdot R sub 1} over {R sub 1 + R sub 2} = {50v cdot 5K%OMEGA} over { 25K%OMEGA} = 10v , then find the polarity by looking at the source: V sub O2 = +10v

Add the two components together: V sub O = V sub O1 + V sub O2 = 8v + 10v = 18v .

Example 2: Find VO.

Isolating each individual voltage source, V sub O = V sub O1 + V sub O2 + V sub O3
abs{V sub O1} = {E sub S1} cdot {1 over {1 over R sub 2 + 1 over R sub 3 + 1 over R sub 4}} over {R sub 1 + (1 over {1 over R sub 2 + 1 over R sub 3 + 1 over R sub 4})} = {40v cdot 2K%OMEGA} over {6K%OMEGA + 2K%OMEGA} = 10v V sub O1 = +10v .
Repeating for each voltage source, we find that: V sub O2 = {-20v cdot 2K%OMEGA} over {6K%OMEGA + 2K%OMEGA} = -5v and V sub O3 = {10v cdot 2K%OMEGA} over { 6K%OMEGA + 2K%OMEGA} = 2.5v .
Having found VO for each voltage source, we can then find the total for all sources: V sub O = V sub O1 + V sub O2 + V sub O3 = 10v - 5v + 2.5v = 7.5v .

Example 3: Finding voltage when a current source is present.

When only ES is active, resistance through IS is infinite, thus it's simply the sum of R1 and R2. V sub O1 = {E sub S1 cdot R sub 2} over { R sub 1 + R sub 2} = {20v cdot 8K%OMEGA} over {12K%OMEGA} = 13. bar 3 v

When only IS is active, the voltage is abs{V sub O2} = I sub S2 cdot ({R sub 1 cdot R sub 2} over { R sub 1 + R sub 2}) = 10 x 10 ^ {-3}A cdot 2. bar 6 x 10 ^3 %OMEGA = 26. bar 6 .
Combine the two components to get: V sub O = V sub O1 + V sub O2 = 13. bar 3 + 26. bar 6 = 40v .

Example 4: Only current sources

When only IS1 is active: V sub O1 = I sub B cdot R sub 4 where IB is the branch we're looking at (containing R3 and R4). V sub O1 = {I sub S1 ( {R sub 2 (R sub 3 + R sub 4)} over {R sub 2 + R sub 3 + R sub 4})} over {R sub 3 + R sub 4} cdot R sub 4 = {40mA cdot 0.9K%OMEGA} over {9K%OMEGA}cdot 3K%OMEGA = 12v

When only IS2 is active: V sub O2 = I sub D cdot R sub 4 where ID is the branch we're looking at. V sub O2 = {I sub S2 ({R sub 3(R sub 2 + R sub 4)} over {R sub 3 + R sub 2 + R sub 4})} over { R sub 2 + R sub 4} cdot R sub 4 = {-5mA cdot 2.4K%OMEGA} over {4K%OMEGA} cdot 3K%OMEGA = -9v
Adding the components: V sub O = V sub O1 + V sub O2 = 12v - 9v = 3v .

Node Equations
Node equation
A current equation (KCL) where the significant unknown quantities are voltages (via Ohm's Law substitutions).
A standardized simultaneous equation methodology with the superposition theorem embedded in it.

Usual knowns: ES1, ES2, R1, R2, R3, R4, R5.
Significant unknowns: VAN, VBN.

Develop Node Equations
Only V sub AN <> 0 (e.g. ES1=0 and VBN=0) and work with only this part of the circuit, using KCL, SSN, Ref A, Sum I from A. I sub 1 + I sub 2 + I sub 3 = 0 which sets the indicated polarity of R1, R2 and R3 such that their positive sides are all at A. Using Ohm's Law: V sub 1 over R sub 1 + V sub 2 over R sub 2 + V sub 3 over R sub 3 = 0 .
Substitute with values that we're looking for (KVL, SSN, Ref N, CW, LPI): -E sub S1 - V sub 1 + V sub 2 = 0 V sub 1 = V sub 2 - E sub S1

Find another substitution value (KVL, SSN, Ref N, CW, LPI): -V sub 2 + V sub 3 + V sub BN = 0 V sub 3 = V sub 2 - V sub BN .
Put the new values for V1 and V3 in place: {V sub 2 - E sub S1} over R sub 1 + V sub 2 over R sub 2 + {V sub 2 - V sub BN} over R sub 3 = 0 . V2 = VAN, so: {V sub AN - E sub S1} over R sub 1 + V sub AN over R sub 2 + {V sub AN - V sub BN} over R sub 3 = V sub AN over R sub 1 - E sub S1 over R sub 1 + V sub AN over R sub 2 + V sub AN over R sub 3 - V sub BN over R sub 3 = 0
V sub AN(1 over R sub 1 + 1 over R sub 2 + 1 over R sub 3) - E sub S1 over R sub 1 - V sub BN over R sub 3 = 0

Looking at the other side of the circuit:

I sub 3 + I sub 4 + I sub 5 = 0 V sub 3 over R sub 3 + V sub 4 over R sub 4 + V sub 5 over R sub 5 = 0
Find some terms to substitute using KVL, SSN, Ref N, CW, LPI:
-V sub AN - V sub 3 + V sub 4 = 0 V sub 3 = V sub 4 - V sub AN
and KVL, SSN, Ref N, CW, LPI:
-V sub 4 + V sub 5 + E sub S2 = 0 V sub 5 = V sub 4 - E sub S2
substitute into the original: {V sub 4 - V sub AN} over R sub 3 + V sub 4 over R sub 4 + {V sub 4 - E sub S2} over R sub 5 = 0 = V sub 4 over R sub 3 - V sub AN over R sub 3+ V sub 4 over R sub 4 + V sub 4 over R sub 5 - E sub S2 over R sub 5
V sub 4 = V sub BN V sub BN ( 1 over R sub 3 + 1 over R sub 4 + 1 over R sub 5) - V sub AN over R sub 3 - E sub S2 over R sub 5 = 0