01.001.0045	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement Math-utility-Coordinate-To-Vector Description: Convert from Cartesian to polar coordinates, Inputs: long int X, Y - The input Cartesian coordinates. struct *VECT_S - The output polar (vector) coordinate structure. Variables Used: No external variables are referenced. Return Value: The function is void - The result is written to the passed structure (angle and magnitude). Variables Updated: No external variables are accessed.
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.001.0046	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement Math-utility-XY-to-SIN-COS Description: Compute Sin and Cos from Cartesian coordinates and phase Inputs: struct *CORD_S - The input/output result structure uint phase - input phase angel Variables Used: No external variables are used Return Value: The function is void - The result is written to the passed structure (sin and cos values). Variables Updated: No external variables are accessed.
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.001.0047	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement Math-Utility-Exponential-Filter Description: A simple exponential decay filter: y(n) = y(n-1) - y(n-1)>>(N-z) + x(n)>>(N-z) Inputs: ulong start_value - the current filter output value. ulong new_value - the new raw input value to go into the filter. uint decay_coefficient - The exponential decay factor/value/rate Variables Used: No external variables are accessed. Return Value: ulong new_filtered_result - The filter output for the given inputs. Variables Updated: No external variables are changed.
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.001.0065	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.065.0132	Category: Timing / Type: Regulatory
HL SW Requirement ( 065 ) The unit shall exit start-up mode within 15 seconds of unit power-up.
LL SW Requirement StartupSafety::_reset_vector__() Description This function overrides the GCC default startup code. It is the target of the unit reset vector. This function executes the low level processor initialization and unit startup/safety checks including: / - initializes the stack pointer / - execute RAM address check, / - execute RAM pattern check / - execute code CCITT-CRC-16 check / - execute configuration CCITT-CRC-16 check / - execute non-volatile-RAM CCITT-CRC-15 check and archive, / - execute .data segment initialization from a code buffer / - paints the stack / - initializes the Flash memory controller and discrete output modules / (to support failure reporting on the AIM_SET LED) / - reads the hardware mode-discrete interlock values / - jump to the main function. / Function Arguments and Return: None. Variables Used: - Code address space 0x1100-0xFBFF & 0xFFE0-0xFFFF is CRCed - Configuration address space 0x1080-0x10FF is CRCed - Non-Volatile-RAM space 0x1000-107F & 0xFC00-FDFF is CRCed Variables Updated: - RAM address space (RAM_START - RAM_END) is checked and initialized - STACK address space (STACK_TOP - STACK_BOT) is painted - sfr WDTCTL - Watchdog timer register is set - sfr P2SEL, P2DIR - Port 2 pin type and I/O select are set for the mode discrete inputs. - mode_buffer - The mode discrete input buffer is set (The mode discretes/hardware-interlocks are read only at startup.)
Req Source:	Software Requirements Document
Reference:	01.065	Paragraph:	3.0
Source:	StartupSafety::_reset_vector__()	Function:	NA
Unit Test Case:

01.066.0088	Category: Timing / Type: Regulatory
HL SW Requirement ( 066 ) The unit shall report input pressure changes (>50 foot altitude and >10 Kt airspeed) within 5 seconds.
LL SW Requirement Altitude-Converter-scheduler-idle-task Description: The idle task watches the clock ticks and sets the modules run state when 62.5ms have elapsed. Inputs: struct *ASC_S - The Altitude module data structure. Variables Used: The clock module CC_getTicks() method returns the "current time". Return Value: No return value Variables Updated: The task state may be set to "1=run". When the task state is set to run the current time is saved in "ulong ticks".
Req Source:	Software Requirements Document
Reference:	01.066	Paragraph:	3.0
Source:	AltitudeComputer::idle	Function:	NA
Unit Test Case:

01.067.0075	Category: Timing / Type: Regulatory
HL SW Requirement ( 067 ) The SADC shall report updated wind speed, wind direction and magnetic heading within 5 seconds of receiving a new heading or ground speed.
LL SW Requirement Winds-Calculator-idle-task Description: The idle task watches the clock ticks and sets the modules run state when 0.5 seconds have elapsed. Inputs: struct *WC_S - This modules private data structure. Variables Used: The clock module CC_getTicks() method returns the "current time". Return Value: No return value Variables Updated: The task state may be set to "1=run". When the task state is set to run the current time is saved in "ulong ticks".
Req Source:	Software Requirements Document
Reference:	01.067	Paragraph:	3.0
Source:	WindComputer::idle	Function:	NA
Unit Test Case:

01.068.0089	Category: Timing / Type: Regulatory
HL SW Requirement ( 068 ) The SADC processor busy percentage shall not exceed 90%.
LL SW Requirement CPU-Monitor-Scheduler-Idle-Task Description: The CPU monitor idle task consumes/reserves a fixed amount of CPU processing time per call and once per second calculates processor idle percentage based on the amount of time reserved in this function. Arguments & function Return: None. Data Used: The "current time" will be read from the clock module Variables Updated: The CPU-Monitor idle percentage value will be updated once per second. The CPU-Monitor idle accumulator will be updated every call.
Req Source:	Software Requirements Document
Reference:	01.068	Paragraph:	3.0
Source:	CPUMonitor::idle()	Function:	NA
Unit Test Case:

01.069.0049	Category: Timing / Type: Regulatory
HL SW Requirement ( 069 ) The SADC unit valid discrete output shall be updated at least once per second.
LL SW Requirement Discrete-output-scheduler-idle-task Description: The disrete-output idle task watches the clock ticks and sets the module to run state (to update the discrete outputs (grey-code, AIM_set, AIM_alt and unit-valid)) every second. The idle task will trigger an earlier run-state/update when either the grey-code or AIM output or unit-valid values change. Inputs: struct *SPC_S - The discrete output module data structure. Variables Used: clock module CC_getTicks() - returns the "current time". AIRDATA->cor_altitude - The current encoder output altitude. this->aim - The aim state buffer set by calls to this modules SPC_set/clrSET() and SPC_set/clrALT() functions. this->unit_valid - The unit valid flag Return Value: No return value Variables Updated: The task state may be set to "1=run". When the task state is set to run the current time is saved in "ulong ticks".
Req Source:	Software Requirements Document
Reference:	01.069	Paragraph:	3.0
Source:	SerialParallelController::idle()	Function:	NA
Unit Test Case:

01.069.0051	Category: Timing / Type: Regulatory
HL SW Requirement ( 069 ) The SADC unit valid discrete output shall be updated at least once per second.
LL SW Requirement Scheduler-Task-Initialize Description: Initialize a scheduler task object. The module variables are cleared and the inputs (the object pointer and number of supported states) are saved. Inputs: struct *TASK_S - The (scheduler) task module private data structure byte number_of_states - The number of states supported by the task. Variables Used: No variables are read. Return Value: void - No value is returned Variables Updated: No external variables are set.
Req Source:	Software Requirements Document
Reference:	01.069	Paragraph:	3.0
Source:	Task::init()	Function:	NA
Unit Test Case:

01.069.0052	Category: Timing / Type: Regulatory
HL SW Requirement ( 069 ) The SADC unit valid discrete output shall be updated at least once per second.
LL SW Requirement Scheduler-Task-Increment Description: This method is called by the main loop after a task returns from the run() method. It will advances the state of the task to the next state. If the current state is the last state, the task is set to the idle state. Inputs: struct *TASK_S - The (scheduler) task module private data structure Variables Used: this->state - The current (private) state is read / incremented / rolled-over as described in the method description. this->num_states - The (private) task number-of-states is read. Return Value: void - No value is returned Variables Updated: this->state - The current (private) state is read / incremented / rolled-over as described in the method description.
Req Source:	Software Requirements Document
Reference:	01.069	Paragraph:	3.0
Source:	Task::next()	Function:	NA
Unit Test Case:

01.069.0053	Category: Timing / Type: Regulatory
HL SW Requirement ( 069 ) The SADC unit valid discrete output shall be updated at least once per second.
LL SW Requirement Scheduler-Task-Setter-Getter-Methods Description: The scheduler module supports nine setter-getter functions: byte TASK_isIdle( *TASK_S) - Is the task in idle state (1=true, 0=false). byte TASK_getState( *TASK_S) - Return the task state value. byte TASK_setState( *TASK_S, byte state) - Set the task state value. --- The Oper(ating) flags functions provide 16 generic bit --- flags to each task. The flag(s) to be set/cleared/checked --- are passed in to each method. byte TASK_checkOper( *TASK_S, int mask) - Are one or more of the passed bit flags set? (1=true, 0=false) uint TASK_setOper( *TASK_S, byte mask) - Set the passed bit flags. uint TASK_clearOper( *TASK_S, byte mask) - Clear the passed bit flags. --- The Error flags functions provide 16 generic bit --- flags to each task. The flag(s) to be set/cleared/checked --- are passed in to each method. byte TASK_checkError( *TASK_S, int mask) - Are one or more of the passed error (bit) flags set? (1=true, 0=false) uint TASK_setError( *TASK_S, byte mask) - Set the passed error (bit) flags. uint TASK_clearError( *TASK_S, byte state) - Clear the passed error (bit) flags. Inputs: All functions input the *TASK_S - This modules data structure The Oper and Error functions have a 16-bit input mask argument. The setState function taks a byte new-state input argument. Variables Used: The only variables accessed are the values returned (see below). Return Value: uint set/clearOper() - Return the operating flags buffer. uint set/clearError() - Return the error flags buffer. byte checkOper/Error() - Return 0=false, 1=true byte getState() - Returns the current task state value Variables Updated: TASK_set/clearOper() - update the private operating flags buffer. TASK_set/clearError() - update the private error flags buffer. TASK_setState() - updates the private task state value.
Req Source:	Software Requirements Document
Reference:	01.069	Paragraph:	3.0
Source:	Task::set/getState()	Function:	NA
Unit Test Case: