01.001.0045	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement Math-utility-Coordinate-To-Vector Description: Convert from Cartesian to polar coordinates, Inputs: long int X, Y - The input Cartesian coordinates. struct *VECT_S - The output polar (vector) coordinate structure. Variables Used: No external variables are referenced. Return Value: The function is void - The result is written to the passed structure (angle and magnitude). Variables Updated: No external variables are accessed.
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.001.0046	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement Math-utility-XY-to-SIN-COS Description: Compute Sin and Cos from Cartesian coordinates and phase Inputs: struct *CORD_S - The input/output result structure uint phase - input phase angel Variables Used: No external variables are used Return Value: The function is void - The result is written to the passed structure (sin and cos values). Variables Updated: No external variables are accessed.
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.001.0047	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement Math-Utility-Exponential-Filter Description: A simple exponential decay filter: y(n) = y(n-1) - y(n-1)>>(N-z) + x(n)>>(N-z) Inputs: ulong start_value - the current filter output value. ulong new_value - the new raw input value to go into the filter. uint decay_coefficient - The exponential decay factor/value/rate Variables Used: No external variables are accessed. Return Value: ulong new_filtered_result - The filter output for the given inputs. Variables Updated: No external variables are changed.
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.001.0065	Category: Derived Requirements / Type: Regulatory
HL SW Requirement ( 001 ) Derived Low-Level software requirements shall be identified and verified
LL SW Requirement
Req Source:	Software Requirements Document
Reference:	01.001	Paragraph:	3.0
Source:		Function:
Unit Test Case:

01.065.0132	Category: Timing / Type: Regulatory
HL SW Requirement ( 065 ) The unit shall exit start-up mode within 15 seconds of unit power-up.
LL SW Requirement StartupSafety::_reset_vector__() Description This function overrides the GCC default startup code. It is the target of the unit reset vector. This function executes the low level processor initialization and unit startup/safety checks including: / - initializes the stack pointer / - execute RAM address check, / - execute RAM pattern check / - execute code CCITT-CRC-16 check / - execute configuration CCITT-CRC-16 check / - execute non-volatile-RAM CCITT-CRC-15 check and archive, / - execute .data segment initialization from a code buffer / - paints the stack / - initializes the Flash memory controller and discrete output modules / (to support failure reporting on the AIM_SET LED) / - reads the hardware mode-discrete interlock values / - jump to the main function. / Function Arguments and Return: None. Variables Used: - Code address space 0x1100-0xFBFF & 0xFFE0-0xFFFF is CRCed - Configuration address space 0x1080-0x10FF is CRCed - Non-Volatile-RAM space 0x1000-107F & 0xFC00-FDFF is CRCed Variables Updated: - RAM address space (RAM_START - RAM_END) is checked and initialized - STACK address space (STACK_TOP - STACK_BOT) is painted - sfr WDTCTL - Watchdog timer register is set - sfr P2SEL, P2DIR - Port 2 pin type and I/O select are set for the mode discrete inputs. - mode_buffer - The mode discrete input buffer is set (The mode discretes/hardware-interlocks are read only at startup.)
Req Source:	Software Requirements Document
Reference:	01.065	Paragraph:	3.0
Source:	StartupSafety::_reset_vector__()	Function:	NA
Unit Test Case:

01.066.0088	Category: Timing / Type: Regulatory
HL SW Requirement ( 066 ) The unit shall report input pressure changes (>50 foot altitude and >10 Kt airspeed) within 5 seconds.
LL SW Requirement Altitude-Converter-scheduler-idle-task Description: The idle task watches the clock ticks and sets the modules run state when 62.5ms have elapsed. Inputs: struct *ASC_S - The Altitude module data structure. Variables Used: The clock module CC_getTicks() method returns the "current time". Return Value: No return value Variables Updated: The task state may be set to "1=run". When the task state is set to run the current time is saved in "ulong ticks".
Req Source:	Software Requirements Document
Reference:	01.066	Paragraph:	3.0
Source:	AltitudeComputer::idle	Function:	NA
Unit Test Case: