Power Frequency Monitor Documentation
Entry # MT2227
Introduction
The Power Frequency Monitor (PFM) is a MicroChip dsPIC30F3012 micro controller based device used for high resolution measurement of AC power frequency. The Power Frequency Monitor communicates easily with a computer using a RS232 interface.
The Power Frequency Monitor is used to measure the frequency of the consumer power. The frequency range is between 30 to 80 Hz with a resolution of 10 KHz. In the USA, the power frequency standard is 60 Hz. In many other regions in the world, the power frequency is 50 Hz. Measuring this frequency accurately can provide an indicator of the relative stability of the local region's power grid compared to that of other non-synchronous regions.
PC software is used to download the data from the Power Frequency Monitor at a desired interval. The data can optionally be uploaded to a database and web server over the Internet to be displayed on a strip chart in a web browser with the data from other Power Frequency Monitors as illustrated by Figure 2.
The MicroChip dsPIC30F3012 micro controller was selected for its integrated input capture peripheral, UART (RS232), SPI (Serial Peripheral Interface), and integrated EEPROM features. The prototypes tested demonstrate that this micro controller has great reliability and performance. The dsPIC30F3012 has also proven to be durable enough to survive the abuse of my learning curve while I developed the prototypes!
System Description
Figure 1, below, is a block diagram of the Power Frequency Monitoring system. The system input is from any standard electrical outlet. Different AC-AC transformers may be used depending on the local electricity outlets and frequencies which vary depending on the country you are plugging into.

Figure 1 – System Block Diagram
The AC input is reduced to 9VAC(rms) by simple transformer. The 9VAC from the transformer is connected to a full wave bridge rectifier and a half wave rectifier. The full wave rectified output is regulated to 5VDC, used to power the system components, and used as a reference voltage for generating the frequency square wave.
The half wave rectifier output “pulses” are fed into an MCP6292 Operational Amplifier. The pulses are converted to a square wave by using the Op Amp as a voltage comparator. When the pulse voltage is less than Vref (about 2.5VDC), the Op Amp's output is 0V. When the pulse voltage is greater than Vref, the Op Amp's output is 5V. The MCP6292 was selected because it provides a 10MHz, high resolution, response. The Op Amp's output is connected to the Input Capture pin on the micro controller. Photo 1, below, shows the conversion of the half-wave rectifier signal to a square wave by the Op Amp.

Photo 1 – Half Wave to Square Wave Conversion
The core component of the Power Frequency Monitor is the MicroChip dsPIC30F3012 micro controller. The micro controller uses an external 12.000MHz clock crystal. The dsPIC30F3012 has an integrated Input Capture peripheral that is configured to generate an interrupt on the leading edge of the square wave signal pulses on the pin connected to the Op Amp's output.
The Input Capture peripheral counts the clock cycles between each leading edge and stores this data in a buffer. The clock cycles are divided by a prescaler of 8 so as not to overflow the 16bit counter in the frequency range being measured. The following equations show that a prescaler of 8 provides a cycle count resolution allowing us to measure the desired frequencies without overflow.
( 1sec / 60Hz * 12,000,000 cycles/sec ) / 8 = 25,000 cycles/Hz
( 1sec / 50Hz * 12,000,000 cycles/sec ) / 8 = 30,000 cycles/Hz
The interrupt service routine (ISR) copies the buffered data to a memory variable so it can be accessed asynchronously by the program loop. The ISR then clears the buffer. The program loop determines what to do with the frequency data based on programmed rules and commands received from the PC. The data is typically transmitted to a PC via RS232 at the PC's request.
Optionally, the data can be stored in an external MicroChip 25xx1024 EEPROM for stand-alone data logging. Since data stream is continuous, stand-alone logging needs a rule set to determine what data is worth storing. Typically the data stored in the EEPROM is unusual samples like frequency spikes and dips. The EEPROM can be also be used to accumulate periodic runtime statistics.
A PC communicates with the dsPIC30F3012 using RS232. The PC software polls the micro controller periodically to get the frequency data. The data can easily be transmitted at speeds of 5 or more samples per second using ASCII and a moderate baud rate of 57,600bps. Faster speeds resulted in increased errors and missed data packets. Each data packet contains a sequence number and the data. The sequence number is used to determine if any packets were missed. Only a 3 wire connection is used and no handshake is performed.
The PC software is relatively simple. The software polls the Power Frequency Monitor at timer intervals and performs the frequency and deviation calculations on the data. It displays the data and can also upload the data to a database over the Internet using a web service. Figure 2, below, shows a screen shot of the PC software polling the micro controller every 200ms and transmitting data to the database web server once per second.

Figure 2 – PC Software Screen Shot
Application
The Power Frequency Monitor is used to monitor the frequency of electric power grids. By distributing the monitors over a wide regional or global area, the relative stability of the power grids can be observed and compared with each other. The Power Frequency Monitor developed here is a very inexpensive and simple way to observe frequency variations at various grid locations on either side of High Voltage DC transmission lines between grids to observe how well the connection endpoints are synchronized. Improving synchronization between grid nodes saves power companies money.
To make a relative comparison between grids of the two different frequencies, 50 Hz and 60 Hz, the following percent deviation calculation is used:
(Measured Hz) – (Perfect Hz) / (Perfect Hz) * 100 = Deviation %
For example, the chart shown in Figure 3, below, shows the Houston Texas frequency (Perfect = 60Hz) compared to the North Island, New Zealand frequency (Perfect = 50Hz). The vertical deviation scaling is +/- 1.0%. The equivalent 60Hz frequency scale is on the left and the equivalent 50Hz frequency scale is on the right side of the chart.

Figure 3 – Power Grid Frequency and % Deviation Chart
The PC software controls the resolution of the data displayed in the chart. If the Power Frequency Monitor, or “Meter”, is on a high speed Internet or LAN connection with the server; the frequency can be sampled at a higher rate than meters with limited connectivity. The chart in Figure 3 shows Meter # 1 sampled at a rate of 1 sample per second, Meters #20 and #90 sampled at a rate of 1 sampler each 10 seconds.
The PC software is also responsible for performing the frequency and deviation calculations. When the data is transmitted from the PC through the web service to the web server’s database, the database assigns a time stamp to the data record. The web server is synchronized to a NIST time server. The actual original sample time will be different depending on latency in communication over the Internet; but samples are all time stamped to the standard NIST time at the time they are received; keeping the data lines on the chart relatively synchronized.
Construction
The Power Frequency Monitor is a relatively simple device to construct and program. Photo 2, below, shows the component layout on a breadboard .

Photo 2 – Power Frequency Monitor Layout
Major components of the Power Frequency Monitor from left to right are: RJ45 interface for a MicroChip ICD2 device programmer/debugger, Reset button, MicroChip dsPIC30F3012 micro controller, Activity Indicator LEDs, 12.000 MHz HCMOS crystal, MicroChip 25LC1024 EEPROM, RS232 Transceiver, MicroChip MCP6292 Operational Amplifier, simple diode half-wave rectifier, LM7805 Voltage Regulator, and simple full-wave bridge diode/capacitor rectifier. Figure 3, below, shows the electrical schematic for the Power Frequency Monitor.
All of the components are standard and readily available. The clock crystal is used to provide a stable reference frequency of 12.000 MHz. The Power Frequency Monitor runs with the micro controller configured with a PLL multiplier of 4 for a speed of 48 MHz. The dsPIC30F3012 has a built in 7.37 MHz oscillator. The external oscillator is used in this project because its frequency is known to be better resolution.
The dsPIC30F3012 is easy to program using the MicroChip In Circuit Debugger (ICD2) and free MPLAB development software and C30 compiler. The C30 source code for this project is included in the accompanying PHzMon_30F3012.zip file.
The PC software was developed using Microsoft Visual Studio with C# and .NET Framework 2.0. The PC Software source code and compiled binaries for this project are included in the accompanying PHzMon_Gateway.zip file.
The web service and database software was developed using ASP.NET and Microsoft SQL Server Express Edition. The live web chart display was developed using ASP.NET and the AJAX library. The chart page runs on Microsoft Internet Information Services (IIS) web server and can be viewed in current versions of contemporary web browsers (older versions and text versions do not support AJAX). The web service, web page source code, and script for creating the database schema are included in the accompanying PHzMon_Web.zip file. Although the web development techniques used in this project are relatively standard, instructions for configuring a secure database web application server are beyond the scope of this project.

Figure 3 – Power Frequency Monitor Schematic
Additional Photos

Photo 3 – Layout with Ground and Power Wires

Photo 4 – Layout with Completed Wiring
Document Revision History
09/29/2007	Schematic and Photos updated
09/18/2007	Source Code File Names added