# Preface to Compression Driver Studies
## Background
The efficiency of direct radiator loudspeakers is fundamentally restricted. The electrical input impedance due to the radiation resistance is small compared to the typical coil resistance and the motional electrical impedance due to the mechanical behaviour. Thus, in order to maintain a high efficiency, a large transduction co-efficient and a low diaphragm mass is required; requirements which, if pursued exclusively, reduce the bandwidth of operation [1,p.319]. In practice, without excessive cost and size and while maintaining reasonable bandwidth, a maximum efficiency in the region of 1% is possible with a direct radiator design.
%eta = {R_r} over {R_e over {BL^2} lline Z_m+Z_r rline^2 + R_m + R_r }	(1.1)

Equation 1.1, expression for the efficiency of an electrodynamic loudspeaker outlined by Olsen [2,p.126,pp.213-222] and clarified in Appendix . With a direct radiating loudspeaker Rr is small in comparison to the other terms, in practice limiting the overall efficiency of the device.

Figure 1.1: radiation resistance of direct radiators in 2π generated by both analytical and numerical calculation. Analytical calculation described in [3 p. 187]. Dome surface of spherical cap is 45degrees from axis to edge. Radiation resistance is normalised by size 10 {%rho c_o %pi a^2} .
Figure 1.1, above, shows the radiation resistance for a piston and dome radiator of the same diameter radiating into 2π steradians. The radiation resistance for the case of the flat piston radiator was calculated using an analytical formulation and also using a numerical model. The agreement between the two is remarkably good.
The numerical formulation has the advantage that it may be applied to more general geometries, such as the dome radiator shown, details are described in ????. The calculated curves indicate that, if the radiators were to move with an equal velocity at all frequencies, the transducer would be more efficient at high frequencies. In practice, the radiating diaphragm is designed to move with approximately constant acceleration by ensuring that the mechanical system is mass dominated in the pass band; the result is that the power output is approximately flat up to ka approx 2 .
Since the advent of electroacoustics, horns have been used to improve the efficiency of transducers, the physical principles of horn behaviour were already well known with understanding culminating in the work of Webster [4]. Horn loading of the radiating diaphragm results in a significant increase in the radiation resistance at low frequencies. In their 1924 paper [5], Hanna and Seplian are possibly the first to thoroughly analyse the behaviour of a horn loaded loudspeaker. They draw attention to the significance of the increased motional resistance experienced by the radiating diaphragm due to the presence of the horn. From equation 1.1 it can be seen that an increase in the radiation resistance leads to an increase in the efficiency[1].
[1] The term Zm, the mechanical impedance of the coupled radiating diaphragm, has a dependence on the square of the radiation resistance (see Appendix ). The efficiency is increased by an increase in the radiation impedance only when the mechanical impedance is dominated by other terms – in practice this condition is normally easily met.
For comparison, Figure 1.2 shows calculations of the radiation resistance of horn-loaded radiators. The increase in radiation resistance, in the region below ka approx 2 and above the horn cut-on frequency ( f_c ), is clearly seen in comparison to the direct radiators. The cut-on frequency can be lowered to extend the region over which the increased radiation resistance is seen, but doing so inevitably increases the physical size of the horn. In practice, there are also other considerations when designing a horn for a particular application, such as size and directivity.
In addition to the numerical calculation of radiation resistance in a truncated exponential horn, an approximate analytical calculation was made for an infinite exponential horn of the same flare rate, as described in [3,p.414]. These two results are shown for comparison below in Figure 1.2. It is interesting to observe the similarity of the calculated radiation resistances above the cut-on of the horn, despite the severe approximations in the analytical calculation. The large difference in the region below the cut-on frequency results predominantly from the truncation of the horn in the numerically calculated case. It is not possible for a wave to propagate below the cut-on frequency in the analytical infinite horn, at low frequencies the acoustic impedance at the throat is purely reactive. Instead, in the case of the truncated horn, we see a gentle transition to the direct radiating case.

Figure 1.2: radiation resistance of piston radiator in 2π baffle compared to exponential horn loading ( size 10 {f_c equiv ka approx 0.35} ). Approximate analytical calculation in infinite horn as outlined in [3,p.414] . Finite horn,terminated in baffle calculated using FEM/BEM.
If the throat area of a horn is decreased, by extending the horn at the throat such that the flare rate is unchanged, the acoustical impedance at the throat is increased in direct proportion to the throat area reduction. However, if a radiator is now placed at the smaller horn throat, the radiation resistance will have decreased if compared to the original case, with larger throat and larger diaphragm. This is because the mechanical load impedance experienced by the diaphragm due to the presence of the horn is related to the acoustical impedance at the throat by the square of the diaphragm area.
In practice overall transducer efficiency is approximately invariant of radiator and throat area in this comparison because the mass of the radiator is also approximately proportional to the diaphragm area. This effect manifests itself in the Zm term of the expression for transducer efficiency (equation 1.1).
It is possible to increase the radiation resistance and efficiency significantly by reducing the size of the horn throat whilst keeping the diaphragm diameter constant. In this case the acoustical impedance at the throat is increased but the transduction coefficient between the of the mechanical and acoustical systems, the diaphragm area, is not affected. In practice, this can be achieved by joining a large diaphragm to a small horn-throat using a small acoustic volume, as depicted in Figure 1.3. Once again we find first mention of this concept by Hannah and Slepian [5] who outline and analyse the benefits of using a large diaphragm and small horn throat to increase efficiency in their 1924 paper.

Figure 1.3: schematic layout of horn driver with large diaphragm, of diameter d2, and small horn throat, of diameter d2, joined by small acoustical volume.
At low frequencies the air chamber is effectively incompressible and the volume velocity on the input side, imparted by the diaphragm, is equal to the volume velocity on the exit side, at the horn throat. As a result, compared to coupling the same diaphragm directly into an equivalent horn with larger throat diameter, the radiation resistance is increased by the ratio of the diaphragm area to the throat area. This arrangement is often referred to as a compression driver, the air volume as the compression chamber and the ratio of the areas is termed the compression ratio, denoted α in this work. The caveat of this approach is that the boost in radiation resistance is only seen while the compression cavity is of insignificant volume and behaves as a simple compliance.
Figure 1.4 shows the numerically calculated radiation resistance for an axially driven dome radiator firstly coupling directly into the throat of a truncated exponential horn and secondly coupled to an exponential horn of the same flare rate but smaller throat diameter via a chamber of air, as depicted in Figure 1.3. For the case with the large diaphragm and small throat, immediately above the horn cut-on frequency we observe the predicted increase in the radiation resistance. However, this increase is only seen while the air chamber is behaving as a simple acoustic compliance; once the cavity begins to become modal the radiation resistance becomes erratic. The driver output can only be extended to moderate frequencies.
In order to increase the frequency range of operation, Wente and Thuras [6] devised a “plug” placed in-front of the radiating diaphragm. The plug keeps the effective volume of the compression cavity to a minimum. In an appendix of the same work [6] they also outline a design criterion for the layout of compression drivers, relating the highest frequency of operation to the maximum difference in acoustical path from diaphragm to horn throat. This type of phase plug design is known as path-length design.

Figure 1.4: Radiation resistance of horn loaded dome radiator with and without simple compression arrangement. Dome surface is 45degrees from axis to edge.
 Horns are truncated exponential with size 10 {f_c equiv ka approx 0.35} .
For case with compression size 10 {%alpha = 10} .

Figure 1.5: The Wente and Thuras Phase Plug.
Significantly, with the introduction of a phase plug, the point of coupling between the horn and the cavity is moved away from the axis of rotation: the eigenfunctions of the cavity all have maxima at the axis of rotation. Phase plugs are now universally used in high frequency compression drivers.
Figure 1.6 compares the radiation resistance of a basic compression driver layout, as shown in Figure 1.5, with an equivalent phase-plugged version. In this case, the phase plug has three evenly positioned channels of unoptimised length and shape. Even with this very rough phase plug design the radiation resistance is improved, in particular the response is usefully extended to higher frequency. However, there remain some large resonant variations in the radiation resistance.

Figure 1.6: Horn loaded compression drivers with compression ratio 10. Simple junction between cavity and horn compared to a simple phase plug. Dome surface is 45degrees from axis to edge.
 Horns are truncated exponential with size 10 {f_c equiv ka approx 0.35} .
In 1953 Bob Smith published a paper describing how the phase plug channels can be arranged such that the modes in the compression cavity are suppressed [7]. This was a very important piece of work in compression driver development but surprisingly it was largely ignored for a number of years before becoming popularised primarily through JBL compression driver designs using Smith's method [7].
Figure 1.7, below, shows the radiation resistance of two phase-plugged compression drivers loaded by a truncated exponential horn. One of the phase plugs is unoptimised the other is designed to Bob Smith's method. It is clearly shown that the irregularity in the radiation resistance is greatly reduced by the Bob Smith design and the potential output bandwidth is extended remarkably compared to the first compression drivers considered in Figure 1.6.

Figure 1.7: Horn loaded compression drivers with compression ratio 10. Simple unoptimised phase plug compared with Bob-Smith phase plug. Dome surface is 45degrees from axis to edge.
 Horns are truncated exponential with size 10 {f_c equiv ka approx 0.35} .
The analysis of Smith concentrates on controlling the acoustic modes of the compression cavity itself, as opposed to resonances occurring in the entire acoustic phase plug structure. In practice one observes that problematic acoustical modes in a complete compression driver, with phase plug and horn or tube loading it, are not restricted to the compression cavity but also occur in the phase plug structure itself. In-fact they cannot be simply separated into those occurring in the cavity and those occurring in the phase plug, the two parts of the driver are well coupled and combined modes are observed. However, the problem can be separated quite readily into these two areas in terms of design. The desired behaviour of the cavity is that of a small perfect acoustical compliance as in the simple lumped model of the compression driver. In order to meet this target it is essential that the modes of the cavity are not excited. The first stage of design is thus to control these modes – as Smith realised. Having ensured that the cavity is behaving simply, the individual phase plug channels are certain to behave well if terminated separately and not joined together at the end of the phase plug. The final aspect of the design is to join the separate channels into the throat of the horn such that each channel observes no change in acoustical impedance at the junction. This is achieved by adjustment of the length and area of the channels. While Bob Smith does not discuss the second part of the phase plug design, design of the channels, it is an essential starting point to have a well behaved compression cavity so undoubtedly he approaches the problem from the correct direction. This is confirmed by the radiation resistance shown in Figure 1.7 which has had very little attention paid to the paths of the phase plug channels.
There have been few further developments on compression driver phase plug design since Smith. In-fact there are a number of subsequent papers and patents which ignore Smith work and incorrectly interpret the behaviour of the compression cavity, most choosing instead to use the Wente and Thuras path-length interpretation [8][9][10][11].
## Introduction to Studies
Modern transducer design relies heavily on numerical finite element method (FEM) simulation for performance predictions [12]. The application of these techniques to compression driver phase-plug design is now relatively common [13,14]. Typically the vibro-acoustical design will be completed with the help of a fully coupled FEM analysis of the moving mechanical parts, the compression chamber, the phase-plug channels, an appropriate horn, the radiating environment (normally 2pi) and often the air in the rear chamber behind the radiating diaphragm. During such analysis the technique of parametrisation is frequently used to allow the geometry to be quickly manipulated and a range of different perturbation investigated. These geometric parameters may be used in conjunction with optimisation techniques [15], this is a powerful tool and, if used effectively, can result in significant improvements. During the course of the design of a compression driver having a 76.2mm diameter titanium dome membrane it was observed that the optimisation routine would consistently alter the geometry away from the Smith channel arrangement. It was generally observed that the optimiser suggested narrower outer channels than suggested by Smith's theory. This observation was the catalyst for this work on compression driver phase plug design. The following section re-visits Smith's work to identify why his channel arrangement appears to be non optimal for real compression driver geometries. The work in this section was presented at the AES convention in New York 2007 [16] and additionally at the IOA reproduced sound conference in Brighton 2008 [17]. These works were co-authored by Mark Dodd, who was responsible for performing the FEM optimisation and much of the illustrative FEM modelling, the analytical analysis was performed by the author.
In addition to the common annular channel compression driver geometry, compression drivers are also sometimes produced with phase plugs having other channel arrangements. One interesting alternative arrangement is the radial channel phase plug. In section the application of a smith-like technique for the design of the phase-plug channels is investigated. This work was presented at the AES convention in San Francisco 2008 [18]. This work was co-authored by Mark Dodd, who was responsible for performing the 3D FEM simulations and the illustrative FEM modelling, the analytical analysis was performed by the author.