NPM – Message Details
This document describes the message details that are passed on the CAN network to the Network Power Module.

Overview
Message Size
All messages are a fixed width of 8 bytes. The CAN specification allows for messages between 1 and 8 bytes, however for simplicity we will always issue 8 byte messages.

Packets

Human Name: / Network Synchronisation Packet / Mnemonic: / NETWORK_SYNCH_PACKET / Header Data / 0xF4	Master → NPM / This is sent by the master at the start of every slot zero. / Slaves are expected to re-synch. / Example Use: / Master will automatically transmit this message. SimTap can also transmit in its slot if necessary / Packet Details: / Byte Description / 0 Header Byte – Always 0xF4 / 1 If this value is = TAP NODE ADDRESS then the packet came from the tap. When the tap is connected to the network, we also need to allow the tap to send synch packets.. / 2:7 Not Used

Human Name: / Slave data write / Mnemonic: / SLAVE_DATA_SET / Header Data / 0xE4	Master → NPM / Writes data to the slave device. Data will usually control a particular function of the NPM / Example use: / We can set the voltage threshold which is required for the CPU within the NPM to allow battery charging. Typically this is 13.8VDC, however we can vary this as appropriate. / Packet Details: / Byte Description / 0 Header Byte – Always 0xE4 / 1 Slave type / 2 Channel / 3:6 Data / B7 / B6 / B5 / B4 / B3 / B2 / B1 / B0 / Checksum / Byte / Data Byte 1 / Data Byte 0 / Slave Addx. / Byte 3 / Slave Addx. / Byte 2 / Slave Addx. / Byte 1 / Slave Addx. / Byte 0 / Header / 0xF0