nb Quidditch – Operating Manual

# Introduction
This manual is designed to familiarise family and friends with the operation of the narrowboat Quidditch.
The layout of the manual is based on distinct areas of the boat as defined in the the Contents. However, as many parts of the boat contain multi-functional features, the end of the manual also contains a comprehensive index which endeavours to list all key items.
We recommend that users familiarise themselves with the manual by using both Contents and Index pages.
If anyone feels that any operational details have been omitted, please contact us by email on nbquidditch@dsl.pipex.com or mobile 07803 955913.
Our aim is to make your use of Quidditch as straightforward as possible.
Enjoy your cruise.

Will, Jane & David Chapman
September 1st 2009

# Bow
The bow is essentially the front, or forward, part of the boat. The pointy bit, as the uninitiated may call it. The bow is the location of a number of functional features:
Gas Locker
The gas locker has self-draining holes emerging just above the waterline. There is a (heavy) lid in the middle of the bow, lift this to locate:
Gas cylinders
There are two 13kg gas cylinders and both must always be connected to the manifold, even if one is empty. The reason for this is that there may be a gas leak from the manifold if only one cylinder is connected. Apart from this vital safety issue, it also makes it much easier to restore a flow of gas if a cylinder runs out.
If gas runs out, use the manifold switch to change to another cylinder, making sure that that you open the tap on top of the cylinder.
NOTE that you should replace the empty cylinder as soon as possible so that there is always one in reserve.
When replacing an empty gas cylinder, note that there is a spanner in the locker – which should be secured with a bit of string for easy access.
First close the round tap on top of the cylinder. Then, using the spanner, loosen the nut on the flexible pipe that leads from the manifold to the empty cylinder – NOTE THAT the thread is REVERSED – it is usually tight and you may need to hit the spanner handle with a lump hammer. (There are two lump hammers on board – one on the starboard shelf in the engine room and the other in the storage space below the step between the well deck and lounge.)
Once the empty cylinder is free, remove it carefully (try to avoid chipping the paint) and take it with you to purchase a full one – if you don't return the empty cylinder the supplier will charge extra. The standard cylinder is RED-ORANGE in colour. DO NOT purchase any other colour cylinder.
Once you have the replacement full cylinder, attach it to the manifold. Tighten the nut (remember, it is REVERSE threaded) but leave the valve closed (you are getting gas supply from the existing cylinder).
Water Inlet
The inlet to the fresh water tank is the rising pipe – covered with a screw cap – that is located between the gas cylinders.
The water tank – which is situated below the well deck - holds about 200 gallons and, if nearly empty, can typically take 45 minutes to fill.
To fill the water tank, remove the screw cap (sometimes needs a tap with the spanner) and place it where it won't slide into the canal (it fits neatly onto the tap of a gas cylinder) and feed in the water hose – usually located under the table in the well-deck. Note that you will need a BW Key to gain access to most water stations. A BW key is attached to the boat key chain.
When the water tank is full, water will over flow into the gas locker and out through the self-draining hole and the over-flowing water is usually enough to alert you that the tank is full (audibly and/or visually).
Early on in your cruise it is a good idea to top up the tank every 2 or 3 days. Under normal circumstances it will last longer but better safe than sorry. After a few days cruising you will get a feel for the amount you are consuming and may be able to top-up less frequently.
Remember, the consumption of water is affected by the number of showers taken and frequency of use of the washing machine and dishwasher.
Manual Pump-Out Kit
If you are in a mood to save money – or need an excuse for 30 minutes exercise - you can keep your eyes open for a pump-out station that is suitable for self-pump-out. These stations are usually located in main urban areas where portable toilets are emptied into the main sewer. The kit consists of a manually operated Whale pump and 2 inch flexible pipe. These stations are generally 'few and far between'.
Anchor Mount
There is a D-shaped anchor mount on the starboard (right-hand facing forward) side of the steel section dividing the bow section from the well-deck (see section on Anchor).
Assemble the anchor according to the instructions contained in the holding bag, attach the warp to the anchor and then use the large D-clamp to secure the anchor and warp to the anchor mount.
Tunnel Light
The tunnel light is mounted on a brass pole rising from the deck of the bow. It is controlled from the cockpit Control Panel.
# Cratch
The cratch comprises the wooden frame that protects the well-deck from inclement weather whilst also adding an additional level of privacy to the well-deck and cabin door.
Cratch Cover
The cratch cover can be rolled up partially or completely in fine weather to give passengers a better view of either side of the waterway. Simply roll up each side and secure with the button down straps that are attached to the upper part of the cover.
# Well Deck
The well-deck is the area between the bow section and the cabin door.
Below-seat Storage Areas
Two built-in cushioned seats run on either side lengthways. The seats can be removed to expose two storage areas that contain miscellaneous items for boat cleaning and maintenance.
Water Tank Access
Access to the interior of the fresh water tank is gained by removing screws of the plate that is set into the floor of the well deck. It is only necessary to gain access if the interior of the tank needs cleaning.
Coffee Table
There is also a built-in folding coffee table in the forward section of the well-deck. The water hose is usually stored beneath but if the hose is removed the table can be lowered by moving the hinged supporting flap beneath it to one side.
The well deck leads to the main cabin door to the boat.
Cabin Door
The main entrance to the boat is via a twin stable door type with glass panes. The door has a standard lock backed up with slide bolts inside the cabin. The door key is attached to the main key ring.
# Lounge
Under Step Storage
There is a step that leads from the cabin door into the lounge area. There is storage space below this step that is used for cruising equipment like windlasses, supplementary fenders and ropes, mooring pins and hooks and a lump hammer. Access by lifting the recessed ring to remove the top of the step.
Behind Step Storage
Behind the step is an area for beer/soft drink storage. The step slides out when the two retaining bolts are released. This area is kept cool by the contents of the water tank and surrounding waterway.
Main Water Pump
The behind-the-step area also houses the pump that distributes cold fresh water to the galley, shower and toilet. This pump can be heard each time a tap is turned on in the galley or head. It relies on a pressure differential between the pump and the taps and occasionally it will run for a few seconds without a tap being opened; this is simply a pressure adjustment and shouldn't happen more than once or twice a day.
NOTE: if it does run frequently without a tap being open, the cause needs to be investigated.
Book Shelf (Starboard)
The starboard shelf (and below) houses reference books, equipment manuals and a music centre. The space below the shelf is also used to store the vacuum cleaner (see below).
Water Pump Switch
Starboard (to the right) of the step – at the back of the space below the book shelf - there is a switch which controls the water pump.
The switch is ON when in pulled-out position, OFF when pushed-in. It is a good idea to switch off the pump if the boat is going to be left for any length of time as any fault will run down the domestic batteries.
NOTE: The area below the book shelf is used to store the vacuum cleaner and replacing the cleaner can result in inadvertently switching off the water pump. This is the first thing to check if water doesn't flow to the toilet or from taps.
Vacuum Cleaner
There is a wet-dry vacuum cleaner stored under the starboard book shelf adjacent to the cabin step. The cleaner runs on 240 volts and should ideally be used when the engine and generator are running.
NOTE: In an emergency, the cleaner can be used to pump out cabin bilge water. To do this, be sure to first remove the dry-use filter.
Television
The TV is runs on 240v and therefore needs the inverter switched on (or engine/generator running). It draws very little current and so is not a severe drain on the batteries (see battery charging).
The indoor aerial is very efficient and by careful directional positioning often works inside. An improved reception is often obtainable by hanging the aerial out of one of the windows or by placing on the coffee table in the well-deck. A better, but less convenient option, is to place the aerial on the roof and thread the lead through the port window.
On arriving at a new mooring, position the aerial to get an initial signal and then use the Menu button on the hand-held to run the automated re-tune. This often finds other channels with a better reception.
Bed Settee
The settee in the lounge opens out into a double bed. Pull the settee away from the wall and 'unfold' the middle section with a mixture of pushing down the back and lifting the seat.
Bedding Storage
Lift the seat of the settee to reveal spare bed sheets, towels, etc.
Life Jackets
There are four life jackets stored with the spare bedding. These should be worn if cruising on rivers.
Anchor
The anchor is stored in a yellow bag kept behind the settee. The anchor warp is kept under the lounge floor boards (See Under Floor Storage).
A chain is not needed as the anchor warp itself is weighted.
Assemble the anchor and warp and attach to the anchor mount in the Bow area (see Anchor Mount in the Bow section)
NOTE: The anchor should be ready for use when cruising on rivers.
Under Floor Storage
On the port side there are two trap doors giving access to under floor (bilge, but dry) storage. Access by lifting the ring pull on each trap door under the rug on the floor of the lounge. This area is used to store the anchor warp and one of the two on-shore power cables. NOTE: The trap doors are quite heavy.
Lounge Cupboards (Port side)
Along the port side of the lounge there are a number of cupboards which are useful for storing items like additional food/drink containers and, in one case, personal items like keys and wallets.
Dining Table
Aft of the settee there is a folding table that can be set up as a dining table.
The Food Chest
Between the settee and the galley there is a heavy duty cabinet of drawers which hold tins and packets of various food stuffs. The top of the cabinet serves as a place to keep books and maps.
Side Hatches
There are two side hatches, one port side in the lounge, the other starboard side opposite the head.
Each hatch is opened by releasing the bolts securing the hatch lid/roof, lifting the roof and pushing open the two hatch doors. Once the hatch doors are open, close the hatch lid again. In the event of rain, there are Perspex window 'panes' stored in the walk-in wardrobe (see reference).
To install a window pane, lift the hatch lid and drop the pane into the slot that runs down each side of the hatch opening. NOTE: The slot keeps the pane from falling out and, when the hatch lid is lowered and re-bolted, prevents casual access (not recommended for extended periods) through the hatch opening.
# Galley
Cooking Area
Hot Drink Makings
The cupboard above the work surface immediately after the lounge area contains mugs and the makings for hot drinks.
Washing Machine
The washing machine is 240 volt and can ONLY be used when the engine and generator are running. The machine cuts out mid-cycle of 240v is not being delivered so it is important to ensure that the engine is running 1500 rpm as shown on the tacometer (see section on Engine Room).
Because of the necessity to ensure that the engine is running at 1500 rpm, ONLY run the washing machine when the boat is stationary. (If the boat is moving, slowing down below normal cruising speed will cause the washing machine to cut out).
Soap etc, is stored in the cupboard below the sink.
Washing Area
# Bunk Room
# Head
# Bedroom
# Engine Room
# Stern