Figure 5: The step sizes of 4 Bit Linear and Companded. The signal has been mathematically reconstructed for missing data.
ELEC2500 Lab 5 Report

First we set up the equipment to show the frame sync signal and the clock pulses, as seen in figure 1.
As can be seen from the picture, there is 8 clock pulses per frame sync signal. This is expected as the sample clock has a frequency of 8.33kHz, which has a period of 120μs. Next we connected a variable DC source to Vin. An example of the result can be seen in figure 2.
Figure 1: Frame sync signal (orange) with clock pulses (blue).
Then, by altering the variable DC, we measured the input voltage and took note of the binary display. The results can be seen in table 1:
Figure 2: The 4 bit output at 0 volts - 1001.
4 Bit Linear			7 Bit Linear
From DC V	To DC V	Binary Value	From DC V	To DC V	Binary Value
	−2.25	0000		−2.52	0000000
−2.25	−1.89	0001	−2.52	−2.47	0000001
−1.89	−1.60	0010	−2.47	−2.43	0000010
−1.60	−1.26	0011	−2.43	−2.40	0000011
			−2.40	−2.37	0000100
				2.38	1111011
1.28	1.60	1100	2.38	2.41	1111100
1.60	1.93	1101	2.41	2.46	1111101
1.93	2.25	1110	2.46	2.51	1111110
2.25		1111	2.51		1111111

Table 1: Step sizes: Comparing 4 Bit Linear and 7 Bit Linear PCM schemes.

Figure 4: An example of 7 bit PCM.
Figure 3: An example of 4 bit PCM.

It can be seen that the average step size for the 4 bit linear is 0.33V, whereas the average step size for the 7 bit linear is 0.04V. This data agrees well with the theory, seeing as there should be 23=8 times as many steps over the same dynamic range, thus the step size for the 7 bit linear should be 1/8 times the size of the 4 bit linear step size. Multiplying the 7 bit linear step size by 8, we get 0.32 V, which is 0.01V less than what we measured.

We then compared the 4 bit linear to the 4 bit companded PCM scheme. The results can be seen below in table 2, with the results also illustrated with the use of a chart – figure 5.
4 Bit Linear			4 Bit Companded
From DC V	To DC V	Binary Value	From DC V	To DC V	Binary Value
	−2.25	0000		−1.250	0000
−2.25	−1.89	0001	−1.250	−0.630	0001
−1.89	−1.60	0010	−0.630	−0.330	0010
−1.60	−1.26	0011	−0.330	−0.150	0011
			−0.150	−0.050	0100
			−0.050	−0.030	0101
			−0.030	−0.011	0110
			−0.011		0111
			0.000		1000
			−0.009	0.030	1001
			0.030	0.083	1010
			0.083	0.162	1011
1.28	1.60	1100	0.162	0.320	1100
1.60	1.93	1101	0.320	0.640	1101
1.93	2.25	1110	0.640	1.300	1110
2.25		1111	1.300		1111

Table 2: Step Sizes: Comparing 4 Bit Linear and 4 Bit Companded PCM schemes. Two elements are missing in the 4 bit companded table as the voltage were too small to be detectable.
It is seen from figure 5, that at the higher magnitude voltages (approximately greater than 0.5 V and smaller than -0.5 V), the linear encoding scheme has a much smaller quantisation error (with is represented by the horizontal length of the steps). At the lower magnitude voltages (the inverse of the previous definition), the companding scheme is a far more accurate encoding scheme (a.k.a. it has a much smaller quantisation error).