HCW
SUSPENSION WEIGHER

- Fully sealed stainless steel load cell
- Mains or battery operation
- Ideal for cranes, barges, sea anchors, load testing.
- Fully assembled ready to install with PT100DI
  Load filtering,
- Peak hold, RS232 option.

Dimensions(Shackle)
Capacity	Model	Order	A	B	C	D	E	F	G	H	I	J	K	L	M
6.5t	HCSW-6.5	HCSW6500S000XX	22	34	53	22	36	78.5	58	157	142.5	107	23	30	42
12t	HCSW-12	HCSW012TS000XX	32	47	74	32	51	109	83	218	191.5	154	31	30	52
25t	HCSW-25	HCSW025TS000XX	45	68	104	45	74	169	126	314	266	226	24	35	63
55t	HCSW-55	HCSW055TS000XX	65	100	145	65	105	245	180	463	358	329	33	35	88

NOTE:	Load cell, shackle, centering sleeve, alignment plate cable and indicator included in ready to install assembly.
Dimensions in mm.

Specifications
Capacity	Model	Order	Display Capacity	Division	Cable	Weight (kg)
6.5t	HCSW-6.5	HCSW6500S000XX	6500	2 kg	10 metres	14.2
12t	HCSW-12	HCSW012TS000XX	12.00	0.01t	10 metres	16.1
25t	HCSW-25	HCSW025TS000XX	25.00	0.01t	15 metres	16.1
55t	HCSW-55	HCSW055TS000XX	55.00	0.02t	20 metres	24

NOTE:	Due to variability in loading circumstances the PT100DI resolution may exceed the accuracy achieved by the shackle.

R70510