Simple DC circuits
Type of networks -
DC
AC – Single phase, polyphase
Common terminologies -
Open circuit – When there's no flow of current throughout the circuit and the reason is an incomplete terminal connection (that is the terminals are open) or a very high off this world resistance in the circuit.
Closed circuit – When the current is flowing happily.
Short circuit – WTF do you mean by a short circuit hu?...its short circuit that's it!...the circuit is too short such that the resistance between the 2 terminals is too low and high amps flows though the circuit burning everything to black ash!
Branch – A section in the circuit necessarily having a component like resistor.
Mesh/loop – A section in the circuit which is closed, that is it forms a loop of current and if separated form the master circuit, its still called a closed circuit.
Voltage and current sources -
Voltage sources -
As the name suggests these sources make constant potential difference across their terminals, that is the power delivery is varied via variation in current rather than the voltage. Here are the subtypes -
Dependent voltage sources -
There's more than what meets the eye in this case. The constant voltage source is backed up or varied beyond/below its rating by another power source which might be a constant current/voltage source.
Independent voltage sources -
You know what it is, to backups for this one, it has to survive the circuit on its own.
Practical voltage sources -
Cause of the internal resistance as the load current increases there's a drop in potential as per the formula V = IR, I don't know why does this drop occur cause of the internal resistance cause it involves electro chemistry, to which I'm unfamiliar.
Ideal voltage source -
No voltage drop...truthful and reliable no matter what the current is and so existence is impossible. A close match is a capacitor.
Current sources -
Here the current remains constant, we can convert constant voltage sources to constant current sources.
An actually current source (not derived from a voltage source) is yet not possible.
Dependent current sources -
Similar to its corresponding subsection in voltage sources...figure it out yourself.
Independent current sources -
Same as the above
Ideal current source -
No matter how high the resistance goes, the current remains constant.
Practical current sources -
Slack in current when its slapped with an insanely high resistance.
Classification of electrical networks -
By presence of source -
Passive – When there's no dedicated current source.
Active – Dedicate current source present.
Direction of current -
Unilateral – The circuit is meant for only one direction of current, usually components like transistorize, diodes etc...are present to give the network such a character.
Bilateral – You know...independent of current direction
Separation of components -
Lumped network – When the components of the circuit are separable, we, students play around with lumped network.
Distributed – When component are not detachable; like in power transmission to our 'holmes'.
Linearity -
Leaner – Simple...if the circuit is invariant to temperate/current/voltage etc changes (that is its resistance, capacitance etc...) and follows ohms law, its linear
Non leaner – Of course!...something opposite!
Circuit simplification techniques -
There are 3 given in the book -
Conversion of parallel/series to one equivalent resistance -
Identify the circuits in parallel and series, add them up and represent one resistance equivalent to them all.
As I said in the Basics of electricty.odt, if the input and output of the resistances are in common, they are in parallel; everyone know how to solve resistances series.
Conversion of delta type series to star and visa versa -
It can be that in some case the previously explained technique fails, here is such a case -

As seen here the resistances R1 and R2 are neither in parallel nor in series...so simplification by conventional techniques is impossible!!
Converting this to -

And the problem suddenly becomes simple!
Refer figures 2.5.1 and 2.5.2
For the delta network, I will call the resistance across the terminals as R'12, R'23 etc... and for the star it'll be Rs12, Rs23...from the figures you can get the resistances.
Generalization -
For delta -
R'_12 = (1 over {R_31 + R_23} + 1 over R_12) ^ -1 = {R_12(R_31+R_23)} over {R_31+R_23+R_21}
R'_13 = (1 over {R_12 + R_23} + 1 over R_31) ^ -1 = {R_31(R_12+R_23)} over {R_31+R_23+R_21}
R'_23 = (1 over {R_31 + R_12} + 1 over R_23) ^ -1 = {R_23(R_12+R_31)} over {R_31+R_23+R_21}
For star -
R^s_12 = R_1 + R_2
R^s_13 = R_1 + R_3
R^s_23 = R_3 + R_2
Delta to star conversion -
Since we want the 2 circuits to be identical in behavior, the resistance across each end should be identical, that is -
R^s_12 = R'_12
R^s_13 = R'_13
R^s_23 = R'_23
Equating the RHS values for each -
For R12
R_1 + R_2 = {R_12(R_31+R_23)} over {R_31+R_23+R_21} ...................1
For R13 -
R_1 + R_3 = {R_31(R_12+R_23)} over {R_31+R_23+R_21} ......................2
For R23 -
R_3 + R_2 = {R_23(R_12+R_31)} over {R_31+R_23+R_21} ............................3
We have to equate these three equations to figure out the values of the equivalent R1, R2 and R3; to do so I'll subtract any 2 of them (for example's sake R12 and R13) and add the resultant to the third -
R_2 - R_3 = {R_12 R_31 + R_12 R_23 - R_31 R_12 - R_31 R_23} over {R_31 + R_23 + R_21} = {R_12 R_23 - R_31 R_23} over {R_31 + R_23 + R_21}
Adding to 3 -
2R_2 = {R_12 R_23 - R_31 R_23 + R_23 R_12 + R_23 R_31} over {R_31 + R_23 + R_21} = {R_12 R_23 + R_23 R_12} over {R_31 + R_23 + R_21}
R_2 = {R_12 R_23} over {R_31 + R_23 + R_21}
So we've got R3 time to find the others...
Substituting the above value of R2 into equation 3 -
{{R_12 R_23} over {R_31 + R_23 + R_21}} + R_3 = {R_23(R_12+R_31)} over {R_31+R_23+R_21}
R_3 = {R_23 R_12+R_23 R_31 - R_12 R_23} over {R_31+R_23+R_21}
R_3 = {R_23 R_31} over {R_31+R_23+R_21}
Substituting value of R3 to equation 2 -
R_1 + {{R_23 R_31} over {R_31+R_23+R_21}} = {R_31(R_12+R_23)} over {R_31+R_23+R_21}
R_1 = {R_31(R_12+R_23)-{R_23 R_31}} over {R_31+R_23+R_21}
R_1 = {R_31 R_12+R_31 R_23-R_23 R_31} over {R_31+R_23+R_21}
R_1 = {R_31 R_12} over {R_31+R_23+R_21}
So we got the final expressions for the conversions -
R_1 = {R_31 R_12} over {R_31+R_23+R_21}
R_2 = {R_12 R_23} over {R_31 + R_23 + R_21}
R_3 = {R_23 R_31} over {R_31+R_23+R_21}
Now convert star to delta -
To do so we got to use the above final expressions, make all combinations of 2-2, multiply all the combinations, and finally divide by R1 then R2 and lastly R3.
Its to be remembered that while dividing both the sides of the equation, the LHS should not be converted to the equivalent delta and the when dividing the RHS it should be converted to its equivalent delta.
R_1 R_2 = {R_31 R_12 ^ 2 R_23} over (R_31+R_23+R_21) ^ 2
R_2 R_3 = {R_12 R_23 ^ 2 R_31} over (R_31+R_23+R_21) ^ 2
R_1 R_3 = {R_23 R_31 ^ 2 R_12} over (R_31+R_23+R_21) ^ 2
Now applying R1R2 + R2R3 + R3R1
R_1 R_2 + R_2 R_3 + R_1 R_3 = {R_31 R_12 ^ 2 R_23 + R_12 R_23 ^2 R_31 + R_23 R_31^2 R_12} over {(R_31+R_23+R_21) ^ 2} ...............1
Dividing 1 by R1 -
R_2 + {R_2 R_3} over R_1 + R_3 = {R_31 R_12 ^ 2 R_23 + R_12 R_23 ^2 R_31 + R_23 R_31^2 R_12} over {(R_31+R_23+R_21)R_31 R_12}
R_2 + {R_2 R_3} over R_1 + R_3 = {R_12 R_23 + R_23 ^2 + R_23 R_31} over {(R_31+R_23+R_21)}
R_2 + {R_2 R_3} over R_1 + R_3 = {R_23(R_12 + R_23 + R_31)} over {(R_31+R_23+R_21)}
R_2 + {R_2 R_3} over R_1 + R_3 = R_23
Dividing 1 by R2 -
R_1 + R_3 + {R_1 R_3} over R_2 = {R_31 R_12 ^ 2 R_23 + R_12 R_23 ^2 R_31 + R_23 R_31^2 R_12} over {(R_31+R_23+R_21)R_12 R_23}
R_1 + R_3 + {R_1 R_3} over R_2 = {R_31 R_12 + R_23 R_31 + R_31^2} over {(R_31+R_23+R_21)}
R_1 + R_3 + {R_1 R_3} over R_2 = {R_31(R_12 + R_23 + R_31)} over {(R_31+R_23+R_21)}
R_1 + R_3 + {R_1 R_3} over R_2 = R_31
Dividing 1 by R3 -
{R_1 R_2} over R_3 + R_2 + R_1 = {R_31 R_12 ^ 2 R_23 + R_12 R_23 ^2 R_31 + R_23 R_31^2 R_12} over {(R_31+R_23+R_21)R_23 R_31}
{R_1 R_2} over R_3 + R_2 + R_1 = {R_12 ^ 2 + R_12 R_23 + R_31 R_12} over {(R_31+R_23+R_21)}
{R_1 R_2} over R_3 + R_2 + R_1 = {R_12(R_12 + R_23 + R_31)} over {(R_31+R_23+R_21)}
{R_1 R_2} over R_3 + R_2 + R_1 = R_12
On further solving the above derived formulas can be written as -
{R_2 R_1 + R_2 R_3 + R_3 R_1} over R_1 = R_23
{R_2 R_1 + R_2 R_3 + R_3 R_1} over R_2 = R_31
{R_2 R_1 + R_2 R_3 + R_3 R_1} over R_3 = R_12
Extracting potential and current on a point in the circuit -
Considering I know the only the P.D across the terminals and the resistance.
In a series circuit -
You know its a piecea cake, first combine all the resistances and figure out the current, then in the main circuit, by application of V = I/R, you can figure out the P.D across each resistance.
Example -

Now if I apply the above technique, P.D across each resistor is a constant.
The total resistance is V = IR1 * 4...so if the P.D is same across each resistance, and their sum will be the actually potential difference; so the potential is getting distributed.
As the resistance increases, the potential along each resistance will drop cause the same potential given by the battery will be have to be distributed more extensively.
In parallel -
Here first get the equivalent resistance, by that figure out i, then by I = v/r you get the individual current through each resistance.
Series after parallel -
How about this -

As said before knowing the potential difference across the battery terminals and the resistance we need to figure out the potential across each resistance.
When an electron leaves the terminal; its at full potential, so to the parallel set it gets all the 1.5v...so when it comes to P.D WRT the other terminal, the parallel set is getting max potential.
Considering the series resistances get added up and represent one resistance which is nothing but in parallel to other resistances, the sum of resistances will get the same max potential of 1.5V; we can now compute the current and we know the resistance expression for the total resistance and finally by application of V = irn, we can get the potential for each resistance.
Parallel after series -

Combine all parallel resistances to 1, which will be in series with the other series set, thereby we'll get elucidated by by the potential difference which the parallel set is getting, and so V will be exposed for all resistances. Since the current passing through the series set is constant, its not a challenge to figure it out, for the parallel set this current will be distributed by I = V/R.
Delta -
Its about figuring out the potential differences/current across 2 terminals.
What we know is the resistance only and not the current across them; and to manipulate current I have to got great depths...so I'll follows the techniques of the book.
Extracting P.D WRT another point -
In series -
We need to know the P.D across each component in the circuit, that way we can reverse engineer the potential difference to the desired point.

Like...suppose the P.D across the R4 is .2, and across R3 is .3...then across the input of R3 to the output of the last R4 will be .5.
Similarly we can combine both the resistances to get .5 as the value.
In parallel -