3GPP TSG SA WG5 (Telecom Management) Meeting #87	S5-130185

Malta, 14-18 January 2013

Title:	[DRAFT] LS on on access network information

Response to:	-

Release:	Rel-8

Work Item:	CH8

Source:	SA5

To:	CT1

Cc:	-

Contact Person:

Name:	Gerald Görmer

Tel. Number:	+49 89 5159 25490

E-mail Address:	Gerald dot Goermer at nsn dot com

Attachments:	none

1. Overall Description:

SA5 discussed the provision of access network information in IMS Charging which received from the access network when PCC architecture is implemented to the P-CSCF but cannot be reported by charging sessions in the originating PLMN.

The P-Charging-Vector carrying the access network charging information is in TS 24.229 not standardized for SIP ACK method. For some scenarios, the ACK is the only available message traversing the P-CSCF that could potentially deliver this charging info to be available in the S-CSCF.

Allowing SIP ACK triggers for the provision will enable errorless correlation between EPC Charging and IMS Charging for subscriber billing as well as for inter-operator accounting.

2. Actions:

To CT1 group.

ACTION: 	SA5 asks CT1 group to confirm this operator requirement.

3. Date of Next SA5 Meetings:

SA5#88	15-19 April 2013	Qingdao,China

SA5#89	27-31 May 2013	Sophia Antipolis,France