## Slide 1
OpenStack® Summit Austin 2016
Headless NFVi for PoP, CO or MSC/MSO
Vinod Chegu
Hrushikesh Gangur

## Slide 2: Agenda
Requirement Description
Can OpenStack meet these requirements?
Mitigation plans
Open items & Discussion

## Slide 3: Requirement Description Problem Statement
Telco use cases do require a multiple-tier NFVi
Point of Presence (PoP) or Central Office (CO) or Mobile Switching Center/Office (MSC/MSO) a.k.a micro DC severely constrained in:
  Space
  Power
  Cooling
Minimal upfront cost
  Control vs. Compute foot print:
Guaranteed bandwidth and latency between Main DC and the micro DC
Centralized operation/maintenance (includes Upgrades)
… ~10K+
Main DC
microDC
microDC
microDC
…~100s
CPE
CPE
CPE
CPE

## Slide 4: Capabilities expected from PoP/CO/MSC/MSO (micro DC)
Predictable performance.
Line rate, Low latency, Low Jitter.
High availability
Persistent data
Networking needs
  reduce round trips to Main DC for FIP/L3/L2 connectivity
Examples of VNFs
vEPC use cases
vRouter
vRAN

## Slide 5: Can OpenStack meet these requirements?

## Slide 6: NFVi w/ CP (VIM) per micro DC : Challenges
Control plane to data plane footprint ratio is out of order
  Few projects focused on virtualizing/containerizing CP to reduce footprint
Centralized maintenance (includes upgrades)
NFV-Orchestration of such discrete and many endpoints is complex
  Quota, Resource management, single dashboard etc.
Overlay networks across VIMs

## Slide 7: NFVi w/o CP (headless) per micro DC : Challenges
A headless micro DC has its CP in the Main DC (aka mothership DC)
Networking requirements for deployment and operations
  L2 connectivity
  Bandwidth (BW)
  Latency
Limiting the data transfer
  Image copy while launch
  Chattiness between CP and computes due to inter-service communication
  Block storage support over WAN
  L3 or FIP connectivity through mothership DC
  Logging and/or monitoring

## Slide 8: Mitigation plans

## Slide 9: Mitigation Plan
#1 Leveraging SDN Solution w/ OpenStack - Pre-requisites
Networking infrastructure to provide
  L2 extension from mothership DC to micro DC (e.g VPLS)
  BW > 2Gbps
  Latency < 80 ms
Preinstalled compute nodes
Cached images on the local compute nodes
Storage array in micro DC for persistent data
HW_VTEP enabled ToR switch
Notes: L2 connectivity is not mandatory, however due to the deployment technologies chosen – like pxe (or preinstalled compute), it needs a same broadcast domain, secondly some of the middleware components like HA of VMs, a multicast traffic is needed
Bandwidth needed for following data transfer requirements:
Images or volume from images
Log collection/monitoring
Latency
Response time between inter-service hand-shake
Posting and picking up messages from the queue
CRUD operation to the database
Preinstalled compute
Ship a preinstalled compute to reduce the install time and reconfiguration
Ideally, configured compute node in the mothership-DC
Cached images
Identified or frequently used images need to be cached on the computes to avoid transfer rate
Storage array
- Volume type relates to compute node

## Slide 10: Mitigation Plans
mothershipDCn
microDCn
Leveraging SDN Solution w/ OpenStack – Reference Implementation – Logical contd.
OpenStack
CTRL
CN
Storage
Array
FIP/L3/L2 VTEP GW
Monitoring/ Logging
CN
CN
CN
CN
Storage
Array
FIP/L3/L2 VTEP GW
CN
Orchestrator
NFV-O
MAN/WAN
vSwitch
SRIOV
SDN
Service Dir
SDN
CTRL
Notes: Availability zone to indicate scheduler to launch in MicroDC computes
vSwitch provides both switching, routing functionality including metadata proxy services
Managing upgrades boils down to upgrading of the compute nodes in the same cloud
Scale

## Slide 11: Mitigation Plans
Leveraging SDN Solution w/ OpenStack – Reference Implementation – Physical contd.
Local Compute and Storage Services
Layer 2 (VPLS,VLAN, VXLAN) Extensions between DC to provide Access to the MGMT Network of the remote DC
MICRO DC is seen as an infrastructure POD attached to the parent DC
DC Management Layer can manage Micro DC resources seamlessly

## Slide 12: Mitigation Plans
#2 Co-exist OpenStack CP w/ Compute + SDN
mothershipDCn
OpenStack
CTRL
CN
SDN
Service Dir
Storage
Array
FIP/L3/L2 VTEP GW
Monitoring/ Logging
CN
CN
CN
Orchestrator
NFV-O
MAN/WAN
microDCn
CN
Storage
Array
FIP/L3/L2 VTEP GW
CTRL w/ CN
SDN CTRL
SDN
CTRL
vSwitch
SRIOV

## Slide 13: Mitigation Plans
#3 Virtualized Control Plane + SDS (Storage) + SDN (Network)
mothershipDCn
OpenStack
CTRL
CN
Storage
Array
FIP/L3/L2 VTEP GW
Monitoring/ Logging
CN
CN
CN
Orchestrator
NFV-O
MAN/WAN
microDCn
CN
KVM Host x3
FIP/L3/L2 VTEP GW
CN
CTRL
SDS
SDN CTRL
SDN
Service Dir
SDN
CTRL
vSwitch
SRIOV

## Slide 14: Open Items
Brainstorm on a few unaddressed problems
#1 Computes w/o CP (headless):
  Deployment of compute nodes in the microDC over WAN
  Low latency monitoring of VNFs
  Image offload
  iSCSI traffic over WAN (boot from volume use cases)
  Underlay L2/L3 VPN connectivity between DCs
  Limit on number of microDCs
#2,3 Computes w/ CP
  Complexity of managing multiple clouds
  Orchestration overhead (user, quotas, provisioning, tenant network setups) using multiple service endpoints, IPAM
Notes: Upgrades
Logging/Monitoring consolidation
Distributed quota management
Global resource view of the tenant
Tenant level Volume/VM migration/backup
Multi-DC image import/clone/export

## Slide 15
Thank you