## Slide 1
SOP No. IM-6017-04
Page 1 of 13
Proprietary and Confidential
1.
Purpose
This SOP describes the procedures to assay the ability of anti-malarial IgG to inhibit the in vitro invasion of RBC and growth of Plasmodium falciparum parasites.
2.
2.1
2.2
SOP Number IM-6017-04 | TITLE Growth Inhibition Assay with Cultured Plasmodium falciparum Parasites | Effective Date 04/13/2015
Revision history
Updated name and location of folders in SHARE-drive Minor editorial revision
3.
3.1
3.2
3.3
3.4
3.5
Definitions
GIA: Growth Inhibition Assay
IgG: Immunoglobulin G antibodies RBC: Red blood cell
ACCM: Complete culture medium for asexual stage culture ICM: Incomplete culture medium
4.
4.1
References
CDC-NIH, Biosafety in Microbiological and Biomedical Laboratories, 5th Edition, U.S. Government Printing Office, Washington, DC, 2007
OSHA Standard -Title 29 CFR1910.1030, Bloodborne pathogens Instruction Manual for the VERSA max Microplate Spectrophotometer
Instruction Manual for the Biological Safety Cabinet, Nuaire, Class II, Type A2
4.2
4.3
4.4
5.
Specific Materials, Instruments and Equipment
See Appendix A: Specific Materials, Instruments and Equipment

## Slide 2
SOP No. IM-6017-04
Page 2 of 13
Proprietary and Confidential
6.
6.1
Safety and Precautions
All work with blood products should be performed in accordance with Biological Safety Regulations. Wear latex or nitrile gloves, a lab coat, and protective eyewear at all times.
All manipulations steps involving human or primate specimens must take place in a biological safety cabinet or in the laboratory with gloves, a lab coat, a mask, and a goggle. Areas and equipment must be decontaminated with 10% bleach (or other approved materials) after use.
Dispose of blood products and other biohazardous materials in the appropriate receptacle.
6.2
6.3
7.
7.1
Procedure
General Notes and Limitation
7.1.1
This SOP is for a GIA with purified IgGs prepared following IM-6018-XX. For other type of samples, consult with supervisor as needed.
This SOP describes the procedure of regular GIA. If an antigen-reversal GIA is performed to test the specificity of GIA activity, consult with supervisor for details.
65% Percoll / 5% Sorbitol synchronization method is described in this SOP. Other methods can be used to prepare a viable synchronized culture of late trophozoites and schizonts for GIA. Consult a supervisor.
7.1.2
7.1.3
7.2
Prepared Stock Solutions
7.2.1
LDH substrate buffer
To prepare 500 mL of the buffer mix 50 mL of 1M Tris-HCl (pH 8.0) and 450 mL H20. Add 2.8 g Sodium L-Lactate. Add 1.25 mL Triton X-100. Mix on a magnetic stirrer at room temperature for at least 30 minutes. Make 50 mL aliquots and freeze at –20°C for up to 1 year.
3-Acetylpyridine Adenine Dinucleotide (APAD) stock solution (10 mg/mL)
To prepare 10 mL of APAD stock solution, dissolve 100 mg of APAD in 10 mL of distilled water. Store the APAD stock solution in 50 μL aliquots in Micrewtubes® at -20°C for up to 2 year
Diaphorase stock solution 50 units/mL
To prepare Diaphorase stock solution, dissolve the 1,500 units Diaphorase vial contents in 30 mL of distilled water. Store 200 μL aliquots in Micrewtubes® at -20°C for up to 2 year.
5% Sorbitol solution
To prepare 100 mL of 5% Sorbitol solution, dissolve 5.0 g of D-Sorbitol in 100 mL of distilled water. Filter prepared solution through sterile 0.2 μm Nalgene filter in the biological safety cabinet. Store 5% Sorbitol solution at 37°C for up to 6 months.
7.2.2
7.2.3
7.2.4

## Slide 3
SOP No. IM-6017-04
Page 3 of 13
Proprietary and Confidential
7.3
Culture and Synchronization of Parasites
7.3.1
General notes: Grow parasites as described in SOP IM-6030-XX. Parasite culture should have late trophozoite and schizont stages just before Percoll synchronization and should have ring or early trophozoite stages for Sorbitol synchronization.
Percoll synchronization
      Prepare 65% Percoll solution. Percoll solution for synchronization must be freshly prepared each time.
        First prepare 90% Percoll solution in PBS by mixing 1 mL of 10X PBS and 9 mL of 100% Percoll. To prepare 65% Percoll solution in PBS, mix 6.5 mL of 90% Percoll/PBS and 2.5 mL of 1X PBS
        Sterilize the solution by 0.2 μm filtering in the biological safety cabinet.
7.3.2
7.3.2.2
Put 5 mL of 65% Percoll solution in a sterile 15 mL tube and place into 37ºC water bath for at least 15 minutes prior to use.
Spin the culture containing late trophozoites and schizonts (e.g., 150 – 200 μL of packed RBC in a 10 mL culture) for 4 minutes at 830g in a 15 mL conical tube.
Aspirate supernatant, leaving 1.0-1.5 mL of medium in the tube. A 10 mL pipet can be used to remove 9 mL of supernatant.
Re-suspend the pellet in leftover medium with a 2.0 mL pipet.
Using same 2.0 mL pipet carefully and slowly overlay culture suspension on 65% Percoll solution in 15 mL tube.
Note: Do not mix or agitate the two layers. Centrifuge at 2,000g for 5 minutes with no brake.
The tube should have a brown layer between the culture medium and Percoll solution. These are late trophozoites and schizonts.
Carefully aspirate medium above the brown layer without disturbing it. Leave approximately 1.0 mL of medium on top of the layer.
7.3.2.3
7.3.2.4
7.3.2.5
7.3.2.6
7.3.2.7
7.3.2.8
7.3.2.9
      Collect the brown layer using 2.0 or 5.0 mL pipet and transfer it into a 50 mL conical tube.
      While gently shaking the 50 mL conical tube, Add drop wise approximately 15 mL of ACCM (or ICM) to the tube.
      Centrifuge for 4 minutes at 830g. Aspirate supernatant, leaving 1.0 –
2.0 mL of supernatant on top of the pellet, because the pellet is very fragile.
      Add, drop wise while gently shaking, 15 mL of complete (or incomplete) culture medium to the 50 mL tube and re-suspend the pellet.
      Centrifuge for 4 minutes at 830g. Aspirate supernatant, leaving 1.0 –
2.0 mL of the supernatant on top of the pellet, because the pellet is very fragile.

## Slide 4
SOP No. IM-6017-04
Page 4 of 13
Proprietary and Confidential
7.3.2.15 Depending on the volume of the parasite pellet, add 200 μL – 600 μL of Prepared O+ RBC (refer SOP IM-6028-XX) and ACCM to bring the suspension to 2 – 3% hematocrit. Put the culture into a new flask.
Sorbitol synchronization
7.3.3
7.3.3.1
Spin the culture for 4 minutes at 830g in a 15 mL conical tube (or a 50 mL conical tube if working with larger volume cultures).
Aspirate supernatant, removing all medium above the pellet (e.g., total volume of pellet left = 200 μL or less).
Using a sterile pipet, re-suspend the pellet in 10 mL of 5% Sorbitol at 37°C for every 200 μL of RBC pellet. If the pellet volume is less than 200 μL, re-suspend the pellet with 10 mL of 5% Sorbitol at 37°C. Mix, using the same pipet. Place the tube at 37ºC for 10 minutes.
Centrifuge at 830g for 4 minutes.
Aspirate supernatant. Re-suspend the pellet in ACCM to 2 – 3% hematocrit and put the suspension into a new culture flask.
7.3.3.2
7.3.3.3
7.3.3.4
7.3.3.5
7.3.4
Example of Time line for Percoll and Sorbitol Synchronization (note: all parasite strains will have varying time lines):
65% Percoll Treatment – Monday 3-5 PM,
Optional Sorbitol Treatment – between 9 PM Monday and 7 AM Tuesday, Sorbitol Treatment – Tuesday 3-5 PM,
GIA assay – Wednesday 1-5 PM
7.4
GIA Worksheet Preparation
Blue and tan colored fields are linked to calculations in other cells. It is very important that no cells are inserted or deleted from the template. Do not edit, paste, cut, or move any well in the tan colored fields.
There are two pages in the form (“Original data” and “Summary”).
7.4.1 Open the GIA Worksheet Form (IM-6017-04-F1), save the file (“file,” “save as”) with a unique name. The format is GIAMMDDYY_XXXn, where XXX are operator’s initials, and n is the nth GIA for the study. As an option, additional working title can be added after the official name in parentheses (e.g., GIA040110_ABD (3D7), etc). Save the worksheet in a study specific folder in “M:\Reference Center\Official Work\GIA\GA or GH” folder.

## Slide 5
SOP No. IM-6017-04
Page 5 of 13
Proprietary and Confidential
7.4.2
Fill in the first worksheet.
Open the first page “Original data”. Fill in (or select one of choices from the list) study number (Excel sheet position B3:D4), the strain of parasite for each plate (C5:D9), whether this assay is a regular GIA or an Ag reversal GIA (C10:D10), and lot # of AMA1-C2 Standard IgG (C11:D11) used.
Plate design
7.4.3
7.4.3.1
Each sample should be tested in triplicates (24 slots per plate). If samples will be tested in singlicate or duplicates for any reason (e.g., the volume of test IgG is limited), consult with supervisor.
Each plate should have one slot of RBC only (uRBC), one slot of infected RBC only (without any IgG, iRBC) and two concentrations of AMA1-C2 standard IgGs (AMA1-C2 Std) in indicated slots below.
Therefore, 20 different test samples can be examined at maximum.
The total volume of each well should be 40 L.
7.4.3.2
7.4.3.3
The GIA plate layout is follows;
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
A | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS
B | iRBC | AMA1-C2 Std 2ul per well | AMA1-C2 Std 12ul per well | Test # 1 | Test # 2 | Test # 3 | Test # 4 | Test # 5 | Test # 6 | Test # 7 | Test # 8 | Test # 9
C |  |  |  |  |  |  |  |  |  |  |  | 
D |  |  |  |  |  |  |  |  |  |  |  | 
E | uRBC | Test # 10 | Test # 11 | Test # 12 | Test # 13 | Test # 14 | Test # 15 | Test # 16 | Test # 17 | Test # 18 | Test # 19 | Test # 20
F |  |  |  |  |  |  |  |  |  |  |  | 
G |  |  |  |  |  |  |  |  |  |  |  | 
H | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS | PBS

## Slide 6
SOP No. IM-6017-04
Page 6 of 13
Proprietary and Confidential
7.4.4
Fill in the plate design
7.4.4.1
Type name of test sample (“Center Code”, B18:B26 and B28:B38), protein concentration of stock IgG (“Stock IgG Conc [mg/ml]”, C18:C26 and C28:C38), volume of test IgG in each well (“Vol of IgG [ul/well]”, D18:D26 and D28:D38). If needed, change the volume of infected RBC solution (“Vol of iRBC [ul]”, F18:F26 and F28:F38) will be added to each well.
Note 1: If a IgG sample will be tested at serial dilutions, type the exact (i.e., as many number of decimal places as possible) calculated volume of stock IgG in the “Vol of IgG [ul/well]” even though the serial dilutions will be done outside of the GIA plate.
Note 2: Whenever needed, use “Note for plate 1” (H15:U18) space for any note for the plate 1.
If GIA with multiple plates is performed, repeat Sections 7.4.4.1 for all other plates (plates 2 to 5).
Note: If more than 5 plates are tested in a single day, make second Worksheet (e,g, GIA010114_ABD2, etc).
Save the .xlsx file (use “save,” do not use “save as”).
7.4.4.2
7.4.4.3
7.5
2X Complete Culture Medium for Asexual Stage Culture (2X ACCM) Preparation
2X ACCM; 20% Human Serum, 2X sodium bicarbonate, 2X gentamicin. The medium needs to be freshly prepared in each assay.
7.5.1
To prepare 50 mL of 2X ACCM, combine 45 mL of ACCM, 1.6 mL of 7.5% sodium bicarbonate solution, 5 mL of processed O+ Human serum (refer SOP IM-6028-XX) and 50 µL of 10 mg/mL gentamicin solution
Filter the prepared solution through sterile 0.2 μm Nalgene filter in the biological safety cabinet
Store at 37°C for up to 8 hours
7.5.2
7.5.3
7.6
Uninfected Red Blood Cell Suspension Preparation
    Prepare 2.0% hematocrit suspension of uninfected RBC in 2X ACCM.
    To prepare 10 mL of 2% hematocrit suspension, mix 400 μL of 50% hematocrit RBC and 9.6 mL of 2X ACCM (Section 7.5).

## Slide 7
SOP No. IM-6017-04
Page 7 of 13
Proprietary and Confidential
7.7
Infected Red Blood Cell Suspension Preparation
7.7.1
Determine parasitemia of synchronized P. falciparum culture (Section 7.3). Parasite culture should have mature trophozoite and early schizont stages just before GIA set-up.
Estimate volume of the culture needed for the assay
Three mL of 0.3 ± 0.1% parasitemia, 2% hematocrit culture is needed for the assay per plate. In addition, 3-5ml more culture is needed for the “parallel culture” (Section 7.8.9).
Transfer the culture into a sterile 15 (or 50) mL tube and spin down for 4 minutes at 830g at room temperature. Aspirate supernatant and re-suspend the pellet to 2% hematocrit with 2X ACCM.
Dilute the 2% hematocrit culture to a parasitemia of 0.3 ± 0.1% with 2% hematocrit suspension of uninfected human O+ RBC in 2X ACCM (Section 7.6).
For example:
Add 6 mL of 2% hematocrit uninfected RBC to 3 mL of 1% parasitemia, 2% hematocrit culture.
Place the tube containing the culture to be used in the assay at 37ºC.
7.7.2
7.7.3
7.7.4
7.7.5
7.8
Assay Set-up
Note1: Assay set-up must be performed in a biological safety cabinet, using aseptic technique, and appropriate laboratory safety attire.
Note2: Final hematocrit in all the assay plate wells should be 1%. The parasitemia at the time of GIA set up should be 0.3 ± 0.1% (excluding wells with uninfected RBC only, uRBC).
7.8.1
Obtain an empty assay plate (Corning #3696 flat bottom sterile 96-well tissue culture plate with lid). Label the plate with study name, parasite line, date, operator and test sample ID, as planned (Section 7.4).
Put test IgG and ICM for each well as planned
Note1: To prevent IgG samples from drying out, consider the order and the way to add these two components into an assay plate (e.g., put ICM first, use multichannel pipettor to shorten the time of transfer, etc)
Note2: To reduce the error of the assay, it is not recommended that less than 5
L of test IgG be handled (especially IgGs with higher protein concentration). In such a case, it may be better to make a dilution of the test IgGs in another sterile 96-well plate, and transfer 5 L of the diluted IgGs to the assay plate.
Put parasite suspension of 0.3 ± 0.1% parasitemia, 2% hematocrit in 2X ACCM (Section 7.7.5) into a sterile multichannel basin. Using 5 – 50 μL Multichannel pipettor and sterile tips, add 20 μL of parasite suspension to all assay wells except wells with uninfected RBC only. Mix the parasite suspension in the basin every time before delivering the parasite suspension to the assay plate.
Add 20 μL of 2% hematocrit suspension of uninfected human O+ RBC to the wells with uninfected RBC only (Section 7.6).
7.8.2
7.8.3
7.8.4

## Slide 8
SOP No. IM-6017-04
Page 8 of 13
Proprietary and Confidential
7.8.5
Using 50 – 300 μL Multichannel pipettor and sterile tips, fill any empty wells of the assay plate (including Row A and H) with 80 μL per well of 1xPBS. Add 80 µL 1xPBS to all inter-well spaces. Cover the plate with a lid.
Place the assay plate in Polypropylene Sealable Bag.
7.8.6
7.8.6.1
Put moistened paper towel or Kimwipes (to provide humidity) in a bag and put the assay plate in the bag.
Using an Electric Bag Sealer, seal the bag, then cut the corner of the bag (2-5 mm)
Inflate the bag by adding mixture gas (5% O2, 5% CO2and 90% N2) through the hole of the bag for 15-30 seconds. Push the bag to release gas, then add mixed gas again for 15-30 seconds.
Completely seal the bag immediately.
7.8.6.2
7.8.6.3
7.8.6.4
Note: If an assay is performed with many plates, a culture chamber can be used, instead of sealing each plate separately.
Place the plate in the sealed bag in a 37ºC incubator until harvest.
If multiple plates are used, perform Sections 7.8.1-7.8.7 for each plate.
Take the remaining volume of parasite suspension, mix with an equal volume of ICM, place in a culture flask with mixed gas, and place in 37ºC incubator.
Note: This parallel culture will be used to help determine the appropriate time of parasite harvest. Do not disturb the flask or change the culture medium in the flask during the course of the GIA.
7.8.7
7.8.8
7.8.9
7.8.10 Record the information in the GIA Worksheet
Open the worksheet prepared in Section 7.4.4. Record the date of GIA assay start (J3:K3), and starting parasitemia (J4:K4). Save the .xlsx file (use “save,” do not use “save as”).
7.9
GIA Harvest
7.9.1
40 – 48 hours (parasite strain dependent) after the GIA assay set up, take the GIA parallel culture flask (Section 7.8.9) from the incubator, make a blood smear, Giemsa stain, and check the growth stage of the parasites for each parasite strain.
Prepare cold 1X PBS.
Take out the assay plate(s) from a 37ºC incubator and open the bag. Put cold1x PBS to a non-sterile multichannel basins just before use.
Using a 50– 300 μL Multichannel pipettor (set to pick up 120 μL), add 120 μL/well of cold 1X PBS to row B to row G of the assay plate.
Centrifuge the plate for 5 minutes at 1,400g at 4ºC with low brake
After centrifugation, using 50 – 300 μL Multichannel pipettor carefully remove 120 μL/well of supernatant out of the assay plate without disturbing the parasite/RBC pellet.
7.9.2
7.9.3
7.9.4
7.9.5
7.9.6
7.9.7

## Slide 9
SOP No. IM-6017-04
Page 9 of 13
Proprietary and Confidential
Note: If at any point a pellet becomes disturbed, repeat the centrifugation.
    Repeat Sections 7.9.5 - 7.9.7.
    Cover the plate with the lid, place the plate on a Titramax-100 platform shaker, and shake the plate for 30 seconds at maximum speed while gently holding the lid of plate.
    After the shake, check whether the parasite/RBC pellets in the all test wells are completely loose. If not, shake the plate for another 30 seconds.
    If multiple plates are used, perform Sections 7.9.3-7.9.10 for each plate, either at the same time, or sequentially (depends on working capacity and number of plates).
    If there is a time constraint and the LDH Assay (Section 7.10) cannot be performed immediately, the plate can be kept at -80ºC for up to two weeks before the LDH assay is performed.
7.10
LDH Assay
NOTE*: NBT is light-sensitive, so avoid direct light and keep solutions and plates with substrate in the dark (cover with aluminum foil).
    Prepare Nitro Blue Tetrazolium (NBT) Solution
      Remove one 50 mL aliquot of LDH substrate buffer from the freezer. Allow the aliquot to thaw slowly to 4°C.
Note: Around 10 mL of NBT solution is needed for a plate (if 18 samples, excluding controls, are tested in the plate)
      Add one NBT tablet (10 mg) into the 50 mL of LDH substrate buffer. Cover the tube with aluminum foil and let it stand for 15 minutes at 4°C. Do not shake, mix gently.
Note: Prepared solution can be kept at 4°C up to 2 weeks in the dark (covered with aluminum foil).
    Warm NBT solution up to room temperature. Wrap the tube with aluminum foil during this step.
Note: If a parasite/RBC plate is kept at -80ºC (Section 7.9.12), warm the plate at room temperature for at least 30 minutes.
    Prepare complete LDH substrate by adding 50 μL of 3-Acetylpyridine Adenine Dinucleotide (APAD) stock (Section 7.2.2) and 200 μL of Diaphorase stock (Section 7.2.3) to every 10 mL of NBT solution.
Note: Complete LDH substrate must be prepared immediately before the start of the LDH Assay. Unused complete LDH substrate can not be stored.
    Using a 50– 300 μL Multichannel pipettor (set to pick up 120 μL), add complete LDH substrate to the wells of the plate (120 μL/well). Start a timer.

## Slide 10
SOP No. IM-6017-04
Page 10 of 13
Proprietary and Confidential
    Spin the plate at 1,800g for 1 min to eliminate bubbles before reading the plate at 650 nm.
Note: Even there is no visible bubbles, spin the plate
    Cover the plate with the lid and keep the plate in the dark.
    At 10 minutes after addition of LDH substrate, place the plate in the Spectrophotometer, shake the plate for 15 seconds and read at 650 nm.
If needed, read the same plate at multiple time points (e.g., 15, 20, 25, 30 min, etc), and report a time point when “infected RBC only” well shows absorbance of 0.4 - 0.6.
Note: Final absorbance can be changed by various factors (e.g., stage of the parasites, parasitemia, parasite strain, etc). Therefore, it may be difficult to predict ideal time point at which a plate should be read in advance.
    Save LDH assay raw data with a unique name. The format is GIAMMDDYY_XXXn, where XXX are operator’s initials, and n is the nth GIA for the study. As an option, an additional working title can be added after the official name in parentheses (e.g., GIA040110_ABD1 (AMA1 in rabbit), etc). Save the pda file in a study specific folder in “M:\Reference Center\Official Work\GIA” folder.
7.11
Calculate % inhibition and Create a Summary Table
    Open the first page “Original data” of the GIA worksheet (Section 7.8.10).
    Type date of LDH assay (J5:K5), final parasitemia (J6:K6), and development time with substrate (J7:K7).
    Copy OD value from the Softmax Pro pda file, select H20 well (green well) in the worksheet for the plate 1, and paste the OD data there.
Note: It is important to paste the data to the appropriate wells. Make sure both the columns and the rows are correct. If not, all data in the Excel template will be wrong.
    Take out well(s) from analysis.
If there is a well(s) for which the operator has an appropriate reason to remove from analysis (e.g., the GIA is performed in duplicates, instead of triplicates), the operator can remove the data of the well.
To remove the data, click the well(s) in J32:U37 and select “remove”, and record the reason of removal in “Note for plate 1” (H15:U18).
    Repeat Sections 7.11.3-7.11.4 for all plates.
    Open the second page “Summary” of the GIA worksheet.
    Type the sample name (i.e., the name used by the sample provider) in Sample name column (C17:C36). Repeat this step for all plates
    Save the .xls file (use “save,” do not use “save as”)

## Slide 11
SOP No. IM-6017-04
Page 11 of 13
Proprietary and Confidential
8.
8.1
Calculations
Use the following formula for percent inhibition:
8.2
Quality check of OD value of each sample: %CV in triplicate
8.2.1
%CV in triplicate is less than or equal to 10 %
If the % of coefficient of variation (%CV) of OD values in triplicate wells is less than or equal to 10 %, the template automatically calculates the % inhibition of a test compared to the OD values in iRBC and uRBC (column E in the “Summary” sheet), and the %CV (column F in the “Summary” sheet).
%CV in triplicate is greater than 10 %
If the %CV of OD values in triplicate wells is greater than 10 %, the form automatically calculates the % inhibition without “outlier” in the triplicate. In such case, the template shows “a”, “b” or “c” in column G in “Summary” sheet and also flags “remove outlier” in column H. “a” means the top well in the triplicates is “outlier” and the template calculates the % inhibition of the test (shown in column E) using the data from other two wells. The %CV value changes to “n/a” in column F. “b” means the middle well is “outlier” and “c” means the bottom well.
If %CV > 10 %, but there is no “outlier”, the template calculates the % inhibition (column E) and %CV (column F) using all three wells, and flags “NI” in column G and “High CV” in column H.
The definition of “outlier” in this template
If there are ODs of “a”, “b” and “c” in triplicates, and %CV of them is greater than 10 %,
8.2.2
8.2.3
Calculate (a-b) ^2, (b-c) ^2 and (c-a) ^2
If maximum value/minimum value > 5 (or minimum value = 0), there is an “outlier”
If (a-b) ^2 is the minimum value, “c” is the outlier, and so on.
8.2.4
If a sample is tested in singlicate or duplicates, and select “remove” in the “Original data” sheet (Section 7.11.4), the template automatically calculates the
% inhibition of a test using the singlicate/duplicates data. But do not calculate
%CV. The template shows “n/a” in column F and the note (either “1 well” or “2 wells”) in column H.
9.
9.1
9.2
9.3
Attachments
IM-6017-04-F1 GIA Template
Appendix A: Specific Materials, Instruments and Equipment Appendix B: Quick reference for Procedure

## Slide 12
SOP No. IM-6017-04
Page 12 of 13
Proprietary and Confidential
Appendix A: Specific Materials, Instruments and Equipment
Note: General materials and equipment (e.g., Distilled water, 12 channel pipette, disposable pipette tips, centrifuges, and personal protective equipment, etc.) are not listed here.
Category | Name | Company | Catalog # | Note
Chemicals and Medium | Incomplete Culture medium | KD Medical | CUS-0645 | 
 | Complete Culture medium for asexual stage culture | N/A | N/A | refer IM-6030- XX
 | Sodium bicarbonate, 7.5% solution | Invitrogen | 25080-094 | or equivalent
 | Gentamicin Reagent Solution, 10 mg/mL | Invitrogen | 15710-064 | or equivalent
 | Percoll | GE Healthcare | 17-0891-02 | or equivalent
 | 10X PBS | Lonza | 17-517Q | or equivalent
 | 1M Tris-HCl, pH 8.0 | Quality Biological | 351-007-101 | or equivalent
 | Triton X-100 | Sigma | T9284 | or equivalent
 | Diaphorase from Clostridium klyiveri | Sigma | D5540-1.5KU | 
 | Nitro Blue Tetrazolium tablets, (10mg/tablet) | Sigma | N5514 | 
 | D-Sorbitol | Sigma | S1876 | or equivalent
 | Acetylpyridine Adenine Dinucleotide (APAD) | Sigma | A5251-100MG | 
 | L (+)-Lactic Acid, Sodium Salt | Sigma | L7022 | 
Instruments, Equipment, Plate and Tubes | Electric Bag Sealer | American International Electric | E188226 | or equivalent
 | Titramax-100 platform shaker, Heidolph Instruments | Thomas Scientific | 8293X01 | or equivalent
 | Sterile 96-well flat bottom half well Tissue culture plates (with lids) | Corning | #3696 | 
 | 0.5 mL Self-standing Micrewtubes® (sterile) | Thomas Scientific | 2591L42 | or equivalent
Other | Prepared O+ Red Blood Cells |  |  | refer IM-6028- XX
 | Processed O+ Human Serum |  |  | refer IM-6028- XX
 | Anti-AMA1-C2 Rabbit IgG Positive Inhibition Standard |  |  | PC-026-00, GIA Reference Center
 | Sterile multichannel basins |  |  | any source
 | Non-sterile multichannel basins |  |  | any source
 | Polypropylene Sealable Bags (used as an Incubation Chamber) | Scienceware | 137080812 | or equivalent

## Slide 13
SOP No. IM-6017-04
Page 13 of 13
Proprietary and Confidential
Appendix B: Quick reference for Procedure
Section Tit | le | Page
7.1 General Notes and Limitation |  | 2
7.2 Prepar | ed Stock Solutions | 2
7.2.1 LDH substrate buffer |  | 2
7.2.2 APAD stock solution |  | 2
7.2.3 Diaphorase stock solution |  | 2
7.2.4 5% Sorbitol solution |  | 2
7.3 Culture and Synchronization of Parasites |  | 3
7.3.1 General notes |  | 3
7.3.2 Percoll synchronization |  | 3
7.3.3 Sorbitol synchronization |  | 4
7.3.4 Example of Time line for Percoll and Sorbitol Synchronization |  | 4
7.4 GI | A worksheet Preparation | 4
7.5 2X | Complete Culture Medium Preparation | 6
7.6 Uninfected Red Blood Cell Suspension Preparation |  | 6
7.7 Inf | ected Red Blood Cell Suspension Preparation | 7
7.8 As | say set-up | 7
7.9 GI | A Harvest | 8
7.10 LDH Assay |  | 9
7.11 Calculate % Inhibition and Create a Summary Table |  | 10