U.S. DEPARTMENT OF AGRICULTURE
NATURAL RESOURCES CONSERVATION SERVICE 
oregon

###### CONSTRUCTION Inspection Plan

##### PIPELINE

Project Description: The pipeline project consists of approximately                  lineal feet of plastic pipeline (PVC) supplying irrigation water at sufficient pressure for irrigation application systems.

Appurtenances included in the pipeline are;

### Items of work to be inspected and timing:

| Timing | Item(s) | Hours* |
| --- | --- | --- |
| Prior to all excavation | Confer with appropriate personnel to review basic requirements and plans |  |
|  | Layout including staking locations of excavation and structures |  |
| Prior to pipe placement | Check alignment, grade and pipeline bedding in excavation including road and creek crossings Inspect pipeline and appurtenances against all materials specifications and requirements |  |
| During pipeline placement and prior to backfill | Confirm pipeline alignment and grade prior to placement of backfill |  |
|  | Check placement and alignment of all structures and fittings. |  |
|  | Check placement of all thrust blocks including alignment and size including on-site inspection during the pouring of thrust blocks. |  |
| Backfill | Inspect backfilling operations including final alignment and placement of pipe and appurtenances |  |
| Installation of valves and controls | Inspect all valves (air relief, air release, vacuum, and control valves) and their installation Inspect placement of vaults and valve covers |  |
| Pipeline filling | Observe pipeline filling including Leaks Structural integrity throughout the system Proper operation of all valves |  |
| Completion of irrigation season | Review pipeline operation with appropriate personnel Inspect pipeline and appurtenances Make sure pipeline draining operations have been completed satisfactorily |  |
| * Includes necessary travel time | TOTAL TIME: |  |

Testing Equipment and Facilities Needed:

Surveying equipment and other miscellaneous equipment.

# Text boxes

| Personnel performing inspections: |  |  |
| --- | --- | --- |
| All inspections will be performed by qualified personnel. |
| Name/ Title: |  |  |  |
| Name/ Title: |  |  |  |

| Approved: |  |  |
| --- | --- | --- |
| Designer |  | Date |
| Basin Engineer |  | Date |
| Basin Team Leader |  | Date |

| Landowner/Operator: |  |
| --- | --- |
| Job Location: |  |
| County: |  | SWCD: |  | Farm/Tract No.: |  |
| Referral No.: |  | Prepared by: |  | Date: |  |