MEMORANDUM

Date:		October 27, 2005

To:		Raj Rao, OAQPS/AQPD/NSRG (MD-C504-03)

From:		Joanne O’Loughlin, Stephen Edgerton, EC/R Incorporated

Subject:	Update of State Minor New Source Review (NSR) Programs

- Purpose

The U.S. Environmental Protection Agency (EPA) is developing Federal minor NSR and nonattainment major NSR rules to fill regulatory gaps in Indian country.  EC/R is supporting the EPA in their regulatory development effort.  As part of that effort, EC/R has done an assessment of selected State Minor NSR Program applicability thresholds (de minimis levels).  The purpose of this memorandum is to present a summary of this assessment.

2.0	Methodology

This assessment includes the review of 23 State air permitting programs.  The 23 State air permitting programs selected are based on a report prepared in 1997 for the EPA on 20 minor source preconstruction air permitting programs (MRI, 1997).  Three additional State air permitting programs are included in the assessment because their websites contained readily-available information on the State’s minor source permitting program.  Our approach was limited to internet searches (e.g., checking for information on the State’s regulatory website(s)) and quick reviews of on-line regulations (where information was not readily-available on a State’s website).  Where we identified minor source applicability thresholds or exemptions, we noted them.  Section 3 summarizes the overall results of our assessment and includes a table indicating the States assessed and whether the State’s program includes minor source applicability  emission thresholds or source/unit exemptions (e.g., gas stations).  Section 4 presents a summary of selected State program applicability emission thresholds and whether they are supplemented by source exemptions.

3.0	State Minor Source Emission Threshold/Exemption Summary Table

The following table presents the 23 State air permitting programs that we assessed and whether they contain minor source thresholds/exemptions.

| State | Minor Source Thresholdsa | Unit/Source Exemptionsb |
| --- | --- | --- |
| Alaska | X | X |
| Arizona (Maricopa County) | X | X |
| California (Feather River Air Quality Management District) | X | X |
| Colorado | X | X |
| Florida | X | X |
| Idaho | X | X |
| Iowa | X | X |
| Kansas | X |  |
| Minnesota | X |  |
| Montana | X | X |
| Nebraska | X | X |
| Nevada |  | X |
| New Mexico | X | X – emissions exemption |
| North Dakota |  | X |
| Oklahoma | X | X |
| Oregon |  | X |
| South Dakota | X | X |
| Texas |  | X |
| Utah | X | X |
| Virginia | X | X |
| Washington | X | X |
| Wisconsin | X | X |
| Wyoming |  | X |

a Minor source thresholds - thresholds, below which a minor source would be exempt.

bUnit/source exemptions – specified unit/source categories that are exempt from having to obtain a permit.

Many of the programs assessed include construction of major and minor sources under the same permitting rules.  Some States subject minor sources to the same permitting requirements as they do major sources.  Some States have permits to construct that, when construction is completed, become the permit to operate.  Some States define a minor source as a non-Title V source that emits any amount of air pollutant, unless declared de minimis or exempted by rule.

Many State air permitting programs have developed minor source permitting programs that attempt to reduce the burden of permitting for minor sources while ensuring that air quality is not adversely impacted (e.g., through the use of pre-approved General Permits, tiered permitting requirements based on the quantity of emissions from a source, exempting small sources from permitting, requiring only registration of minor sources or a subset of minor sources).

The focus of our assessment was to identify existing de minimis emission thresholds and whether there are exemptions for specific source categories of minor sources under the assessed State air quality permitting programs.  Many of the State programs include a long list of exempt source categories/emission units, in lieu of (e.g., Wisconsin has a list of over 100 exempt source categories), or in addition to, de minimis exemption emission thresholds (e.g., Colorado includes both emission thresholds and source category exemptions).

4.0  	Minor NSR State Program Applicability

The following paragraphs present a brief summary of the applicability of minor NSR for 23 State air permitting programs.

Alaska

Since the 1997 MRI Report, the Alaska Department of Environmental Conservation completed an overhaul of their permitting rules in late 2004.  New rules were issued for minor construction permitting.  The minor permit program is for new or relocated minor sources and changes at both major and minor stationary sources.  It would also apply to continued operation of stationary sources not subject to Title V.  Once issued, the general permits and permits by rule would allow an owner or operator to construct and operate a stationary source with little or no delay after submitting an application.

Any stationary source meeting emission rate criteria would need a minor permit for construction or modification if it does not need a major construction permit.

Additionally, the new list includes new stationary sources with allowable emissions greater than:

- 15 tons per year (tpy) particulate matter less than 10 micrometers (mm) in diameter (PM10);

- 40 tpy nitrogen oxide (NOx);

- 40 tpy sulfur dioxide (SO2);

- 0.6 tpy lead (Pb); and

- 100 tpy carbon monoxide (CO) within 10 kilometers (km) of a nonattainment area.

For stationary sources that are required to have a minor permit, a modification that will cause an increase in allowable emissions greater than:

- 10 tpy PM10;

- 10 tpy NOx;

- 10 tpy SO2; and

- 100 tpy CO within 10 km of a nonattainment area.

The permit content regulations for minor permits for air quality protection are designed to allow the department the flexibility to include conditions in their permit application only when they are necessary.  The conditions could include testing, monitoring, record keeping, or reporting.  To satisfy the requirement for a minor permit classified under 18 AAAC 50.502, the owner or operator would have a choice of source specific permits, general permits, or permits by rule.  Although technology review is routinely conducted as part of the permit application process, the State regulations do not specify a specific technology review process.

The department has established a general minor permit for portable oil and gas drilling.  The department may establish additional general minor permits that meet the conditions and requirements for minor source permits, provided there is notice and an opportunity for public comment and hearing.

Source:	http://www.state.ak.us/local/akpages/ENV.CONSERV

Arizona

Maricopa County:

Maricopa County (Phoenix Area) has supplementary regulations to Arizona State regulations.  The program for minor sources is under their non-Title V source permitting requirements.  A “non-Title V source” is “any source other than a major source, including an area source, subject to a standard, limitation, or other requirement under Section 111 or 112 of the Act.”  General emission thresholds for non-Title V permits are total uncontrolled emissions of 3 pounds per day (lbs/day) volatile organic compounds (VOC) and 5.5 lbs/day of any other regulated air pollutant.  Other thresholds include: (1) new or modified sources expected to emit 10 tpy or more of a hazardous air pollutant (HAP) or 25 tpy or more of any combination of HAP designated by the Director and not listed in Section 112(b) of the Clean Air Act (CAA); and (2) non-major sources, including area sources with the potential to emit (PTE) with controls at leas 1 ton, but not less than 10 tpy of a HAP or at least 2.5 tons, but less than 25 tpy of any combination of HAP.  In addition, Maricopa County has established non Title V process thresholds for specific equipment (MRI, 1997).  There have been no changes to these thresholds since the 1997 MRI report.  Major and minor sources are subject to the same permit requirements.  A source may request approval for the classification of an activity as insignificant by including such a request in its permit application.  A list of insignificant activities (activities and units exempt from permitting) (e.g., food processing equipment, surface coating an printing equipment, laboratories and pilot plants) is available in MCAQD Rule 200(1a) and Appendix D (1b).

General permits have been established for the following: dry cleaning, graphic arts operations, gasoline dispensing operations, surface coating operations, vehicle and mobile equipment refinishing operations, and external fuel burning operations.  Specified criteria must be met to be eligible for a general permit.

Source:	http://www.maricopa.gov/aq/divisions/engineering/nontitlev.aspx

California

The California NSR program is derived from the California CAA NSR requirements arising from the California CAA, and are codified in the California Health and Safety Code at Division 26.  Specific to NSR, each District is to include in its attainment plan, a stationary source control program designed to achieve no net increase in emissions of non-attainment pollutants or their precursors for all new or modified sources that exceed particular emission thresholds.  In addition, most new and modified stationary sources are required to use BACT.  In California, BACT is synonymous with the federal term LAER for non-attainment area permit requirements.

Each of the 35 Air Pollution Control Districts in California has its own NSR program and issues its own NSR or PSD permits to construct and operate.  To do so, each district has adopted its own rules and regulations to comply with State and federal laws.  These regulations usually incorporate both the California and federal regulations into one or more rules.

Some of the County Air Pollution Control Districts (also referred to as Districts) have specified exemption (limits for units/source categories), while others do not have specified exemptions from minor source permitting (e.g., Amador County).  It is often at the discretion of the permitting authority to exempt a unit (e.g., if it has a PTE less than 1 tpy) from permitting.  Some Districts require a permit by limit and do not require BACT, while others require BACT (e.g., Antelope Valley requires BACT for minor sources that have a PTE of 25 lbs/day of a criteria pollutant;  Bay Area requires BACT for sources with potential emission of 10 lbs/day of any criteria pollutant) and/or permit limits in lieu of BACT (e.g., Antelope Valley may require that a source that emits less than 25 lbs/day of all criteria pollutants to receive limits based on the permitting official’s discretion; Bay Area requires sources that do not trigger BACT to meet limits for SO2, NOx, CO, and opacity).  Some Districts require that sources that do not trigger BACT (because of a specified emission level) meet reasonably available control technology (RACT) (e.g., Calaveras County requires BACT for sources with a PTE of 15 lbs per hour (lbs/hr) or 150 lbs/day of any criteria pollutant, and RACT for sources that do not trigger BACT.  In some Districts, BACT is case-by-case (e.g., Northern Sierra, North Coast Unified).

Feather River Air Quality Management District:

The 1997 MRI report reviewed the permitting requirements of the Feather River Air Quality Management District (FRAQMD).  The FRAQMD has areas that have severe nonattainment air quality for ozone.  All minor sources that have the PTE greater than 25 lbs/day day of a criteria pollutant are required to apply BACT.  There is a de minimis exemption for a source that has a PTE 2 lbs/day or less of a criteria pollutant.  Other specific source exemptions are specified (e.g., air conditioners, steam cleaning equipment).

Sources:	http://www.arb.ca.gov/nsr/nsr.htm

http://www.arb.ca.gov/drdb/fr/cur.htm

Colorado

All sources of air emissions in Colorado are required to obtain a construction permit unless they are specifically exempted by the provisions of Regulation No. 3.  The Construction Permit Unit issues construction permits to commercial and industrial air pollution sources in Colorado in order to ensure compliance with air quality regulations.  The permitting process and requirements involve a two-phased approach.  The first phase requires the source to report air emissions through the submission of an Air Pollutant Emission Notice (APEN).  In general, an APEN is required for an emission point with uncontrolled actual emission of any criteria pollutant equal to or greater than 2 tpy in attainment areas, 1 tpy in nonattainment areas, and

100 lbs/year of Pb in both attainment and non-attainment areas.  For sources with air emissions exceeding permitting thresholds, the second phase involves the issuing of an air permit.

All construction permits for new or modified sources will be issued for the level of production/operation requested on the APEN.  Minor and major sources are regulated under the same permitting requirements.  The Colorado air permitting requirements outlined here have not changed since the 1997 MRI report.

In general, a construction permit is required for a facility with uncontrolled actual emissions of any criteria pollutant equal to or greater than the following in non-attainment areas:

- 2 tpy of VOC;

- 1 tpy of PM10;

- 5 tpy of total suspended particles;

- 5 tpy of CO;

- 5 tpy of SO2;

- 5 tpy of NOx;

- 200 lbs/year of Pb; and

- 2 tpy of other criteria pollutants.*

For attainment areas, these levels are:

- 5 tpy of VOC;

- 5 tpy of PM10;

- 10 tpy of total suspended particles;

- 10 tpy of CO;

- 10 tpy of SO2;

- 10 tpy of NOx;

- 200 lbs/year of Pb; and

- 2 tpy of other criteria pollutants.*

*Other criteria pollutants – fluorides, sulfuric acid mist, hydrogen sulfide, total reduced sulfur, reduced sulfur compounds, and municipal waste combustor emissions.

Exempt sources categories are specified in Regulation 3, Part B (II.D.) (e.g., specified internal combustion engines, specified gasoline stations located in ozone attainment areas).  None of the exemptions listed in Sections II.D. 1. through II.D.4 shall apply if a source is subject to Part A of Regulation 6 (new source performance standards (NSPS)) and/or Regulation No. 8 (HAPs), Parts A, C, D, and E.  Permit exemptions taken under this section do not affect the applicability of the regulations to the source.  Section II.D.8 states that “any person may request the division to add source categories to the permit exemption list, in accordance with” specified procedures.

Source:	http://www.cdphe.state.co.us/ap/conperm.asp

Florida

A minor source facility is defined as any pollutant source that is not a major source facility.  A “major facility” is defined as a facility that emits or has a TPE 5 tpy or more of Pb or Pb compounds, measured as elemental Pb; 30 tpy of acrylonitrile; or 100 tpy or more of any other air pollutant subject to regulation under Chapter 403, Florida statutes.  Florida includes a long list of source/unit/activity permit exemptions (e.g., vacuum pumps in laboratory operations, equipment used for steam cleaning).  Categorical exemptions are listed in 62-210.300(3)(a).  Generic and temporary exemptions are listed in 62-210.300(3)(b).  The generic and temporary exemptions paragraph includes the following de minimis thresholds:

Generic Emissions Unit Exemptions:

Unit must not emit or have the potential to emit -

- 500 lbs/yr of Pb and Pb compounds expressed as Pb;

- 1,000 lbs/yr of any HAP;

- 2,500 lbs/yr or more of total HAP; or

- 5 tpy or more of any other regulated pollutant.

Generic Facility Exemptions:

The facility would neither emit or have the potential to emit -

- 1,000 lbs/yr of Pb and Pb compounds expressed as Pb;

- 1 tpy of any HAP;

- 2.5 tpy or more of total HAP;

- 25 tpy or more of CO, NOx, and SO2; or

- 10 tpy or more of any other regulated pollutant.

Florida also contains generic non-Title V general permits for minor sources of air pollution, such as mercury recovery and reclamation, bulk gasoline plants, heating units and general purpose internal combustion engines, surface coating operations, plastic products fabrication, cast polymer operations, concrete batching plants, human crematory, animal crematory, and nonmetallic mineral processing plants.

Source:	http://www.dep.state.fl.us/air/permitting/nontv_gp.htm

Idaho

Idaho’s Department of Environmental Quality Air Quality Division requires that an air quality permit to construct prior to construction or modification of a stationary source such as building, structures, and other instillations that emit, or may emit pollution to the air.  A permit to construct is also required for certain portable equipments such as generators.  A major source is a facility that has the PTE 10 tpy or more of any HAP or 25 tpy of any combination of HAP, with exceptions; a facility that directly emits or has the PTE 100 tpy of any pollutant; a facility located in a “serious” PM10 nonattainment area that has a PTE of 70 tpy or more of PM10; a facility in a “serious” CO nonattainment area that has a PTE of 50 tpy or more of CO; a facility located in an ozone transport region that has a PTE of 50 tpy or more of VOC or NOx in excess of specified amounts in marginal, serious, severe, and extreme nonattainment areas.  Minor sources are sources that are not major sources.  Commencing construction of a major facility or major modification prior to obtaining a Permit to Construct is a violation.  Minor sources, on the other hand, may be able to obtain a 15-day pre-permit construction approval.

General exemption criteria are specified in Section IDAPA 58.0101.220.  It states that no permit to construct is required for a source that satisfies all of the general exemption criteria (e.g., source has a PTE less than 100 tpy of any regulated pollutant, emissions increase does not exceed significant emission rates) in addition to criteria set forth in Sections 221, 222, or 223.  Exemptions are also specified for some Category I sources (e.g., sources that have de minimis emissions of less than 10 percent of the significant emission rates specified in Idaho State regulations) (Section IDAPA 58.0101.221) and Category II sources (e.g., sources that have a PTE less than 100 tpy of any pollutant, and qualify as a listed exempt source, such as laboratory equipment used exclusively for chemical and physical analysis)(Section IDAPA 58.0101.222).

Source:	http://www.deq.idaho.gov/air/permits_forms.cfm

Iowa

Iowa’s Department of Natural Resources (DNR) requires that all stationary air pollutant emitting equipment constructed or modified after September 23, 1970 must obtain an air construction permit prior to construction or modification.  This is true for all stationary equipment with air pollutant emissions that could reasonably be captured and vented to the atmosphere through a stack, chimney, vent, or other functionally-equivalent opening, unless exempted as a “small unit.”  A “small unit” is defined as an emissions unit (and associated control equipment) that emits less than the small unit thresholds (specified in 567 IAC 22.1(2)w(1)) on a 12-month rolling total basis.  The emission thresholds are:

- 5 tpy SO2;

- 5 tpy NOx;

- 5 tpy VOC;

- 5 tpy CO;

- 5 tpy particulate matter (PM);

- 5 tpy HAP;

- 2.5 tpy PM10; and

- 40 lbs per year of Pb and Pb compounds expressed as Pb.

An emission unit is defined as any activity or part of an activity that emits or has the potential to emit any pollutant subject to regulation under the CAA.

Any facility may use the exemption provided that the emission units are not subject to federal air requirements (e.g., NESHAP, NSPS, etc.).

The owner or operator must maintain an exemption justification document on site for each emission unit or group of similar emission units that the exemption is being applied to.  The exemption justification document is to include the minimum information necessary to justify the exemption (567 IAC 22.1(2)w(3)).  The exemption justification document is like a permit that the owner or operator writes for the facility stating how their unit or units will be maintained to remain below the small unit emission thresholds.  If an exemption document is not prepared, an air construction permit application will need to be submitted (even when emissions are below the small unit emissions exemption).

An owner or operator must apply for air construction permits for all substantial small units for which the cumulative notice threshold for the pollutant(s) in question has been reached.  These cumulative notice threshold levels are:

- 40 tpy SO2;

- 40 tpy NOx;

- 40 tpy VOC;

- 100 tpy CO;

- 25 tpy PM;

- 10 tpy of any HAP;

- 25 tpy and combination of HAP;

- 15 tpy PM10; and

- 0.6 tpy of Pb and Pb compounds expressed as Pb.

(567 IAC 22.1(2)”w”(8))

Iowa also specifies exemptions under 567 Iowa Administrative Code (IAC)22.1(2) (e.g.,  manually operated equipment and non-production equipment and equipment vented indoors).

Source:	http://www.iowadnr.com/air/prof/const/const.html

Kansas

State “Construction Permits” are required for the following:

- New sources with emission of a regulated pollutant above state PTE threshold (see below);

- Modification of existing source if increase of regulated pollutant emissions exceed state permit PTE threshold;

- Affected Title V sources; and

- Incinerators.

State Permit PTE Thresholds

- 25 tpy PM;

- 15 tpy PM10;

- 40 tpy SOx;

- 100 tpy CO;

- 40 tpy VOC;

- 40 tpy NOx;

- 0.6 tpy Pb;

- 10 tpy HAP; and

- 25 tpy combined HAP.

State Construction Approvals are required for the following:

- New source with emission of regulated pollutant above state approval PTE threshold (see below);

- Modification of existing source if increase of regulated pollutant emissions exceeds state approval PTE threshold;

- Most minor NSPS, Part 61 national emission standards for hazardous air pollutants (NESHAP) and Part 63 NESHAP sources;

- Sources which apply and qualify for an approval under K.A.R. 28-19-302(c)(see below).

State “Construction Approval” PTE Thresholds

- 5 lbs/hr PM;

- 5 lbs/hr PM10 (agricultural);

- 2 lbs/hr PM10 (other);

- 2 lbs/hr SO2 or sulfur trioxide (SO3);

- 50lbs/24 hr period CO;

- 50 lbs/24 hr period VOC (except in Wy or Jo counties);

- 15 lbs/24 hr period VOC or 3 lbs/hr VOC (Wy or Jo counties);

- 50 lbs/24 hr period NOx;

- 0.1 lbs/hr Pb or Pb compounds;

- 50 megagrams/yr non-methane organic compounds (NMOC) (landfills > 2.5 million megagrams or > 2.5 million cubic meters)

K.A.R. 28-19-302(c)

- Allows most sources with actual emissions below State permit thresholds to be treated in the same manner as a source with potential emissions below those thresholds.

- A restriction in an approval will reduce the PTE for State purposes if the reduced PTE is not for the purpose of avoiding PSD or a Class I or II operating permit.

Sources:	KDHE, Bureau of Air and Radiation, Construction Permits and Approvals: Informational Sheet, K.A.R. 28-19-300(a)

http://www.kdheks.gov/air-Permit/forms/Informational_Sheet.pdf

Minnesota

Construction permits are issued for the construction of a new facility whose PTE is over federal or state thresholds, or the modification of an existing facility.  In general, a facility that does not already require a total facility permit will not need a construction permit for a modification at its facility unless the additional PTE of the construction activity increases the PTE of the total facility to the point that the PTE of the total facility crosses a permitting threshold.  State total facility PTE thresholds in tpy are as follows:

- 100 tpy NOx;

- 50 tpy SO2;

- 100 tpy VOC;

- 100 tpy PM;

- 25 tpy PM10;

- 100 tpy CO;

- 0.5 tpy Pb;

- 10 tpy of one HAP; and

- 25 tpy of more than one HAP.

Sources that have a PTE less than 50 tpy of SO2, 25 tpy of PM, 0.5 tpy of Pb and 100 tpy of other criteria pollutants are exempt from permitting if located at a new site.  No State notification is required for these units.  Sources that choose to keep its emissions below these limits will get a registration permit.  If a new unit will be installed at a facility that has already triggered permitting, the new unit can still avoid a permit if (federal) NSR does not apply and the unit’s potential emissions are below the following rates:

- 2.28 lb/hr NOx, SO2, or VOC;

- 0.855 lb/hr PM10;

- 5.70 lb/hr CO; or

- 0.025 lb/hr Pb.

General Permits:  The State permits are similar to the federal permits for “general permits” except that the PTE for those facilities are below the federal thresholds.  There are two available “general permits”: non-metallic mineral processing, general manufacturing.

Registration:  These are for facilities with low actual emissions versus their potential emissions.  In general, the facility’s actual emissions must be less than 50 % of the federal thresholds.  There are other requirements.  These permits are similar to general permits in that they are easier to obtain and the requirements are less rigorous when making modifications.

Minnesota does not specifically define a “minor source,” a permit must be obtained for any new or modified source that has a PTE greater than 50 tpy SO2 (federal major source threshold is 100 tpy), 25 tpy PM10 (federal major source threshold is 100 tpy) and 0.5 tpy Pb (federal major source threshold is 10 tpy).

Source: 	http://www.pca.state.mn.us/air/permits/index.html

Montana

Montana regulations require construction permits for both major and minor sources.  Montana’s major source thresholds are 250 tpy of any criteria pollutant in attainment areas, and 100 tpy in nonattainment areas.  Minor sources are sources that are not major sources.

A minor source facility is required to obtain a minor source permit at a new site if the source has a PTE more than 25 tpy of any criteria pollutant, and a PTE more than 15 tpy of any criteria pollutant for a new or modified source at an existing site (except for Pb).  Under both of these scenarios, the facility would need to complete a State level BACT analysis.  Note that Montana also specifies a long list of exempt units/sources (e.g., agricultural and forest prescription fire activities, food service establishments).  See Administrative Rules of Montana, Sub-Chapter 9, 17.8.743-4.

Montana may adopt rules for the registration of certain classes of sources of air contaminants in lieu of a permit application.

Sources:	http://data.opi.state.mt.us/bills/mca/75/2/75-2-211.htm

Permit Requirements for Major Stationary Sources or Major Modifications Locating Within Nonattainment Areas, Air Quality, Administrative Rules of Montana, Sub-Chapter 9.

Nebraska

Nebraska regulations pertaining to preconstruction permits can be found in Chapter 17, Title 129, Department of Environmental Quality.  The operating permit, which is submitted, reviewed, and approved, also incorporates the construction permit.  Nebraska requires all new or modified sources that emit air pollutants at specified levels to apply for a construction permit.  Nebraska requires both Class I (major sources) and Class II (essentially minor sources) permits.

Threshold limits for source permitting (and de minimis exemption thresholds):

- 15 tpy PM10,

- 40 tpy SO2, NOx, VOC,

- 50 tpy CO,

- 0.6 tpy Pb,

- 2.5 tpy any single HAP, and

- 10 tpy any combination of HAP.  (Chapter 17 of Title 129)

No notification is required for sources that fall below the de minimis thresholds, but it is recommended.  Emission records must be kept.

A minor source construction permit is required for units that emit more than the de minimis exemption levels, or for sources not specifically exempt under Nebraska law (e.g., refuse incinerators on residential premises containing five or fewer living units and used only for residential waste).

Subject minor sources are required to apply BACT.

Sources:

http://www.deq.state.ne.us/Publica.nsf/lddd539d2b73986256870007b30a8/e85cc52a7

http://www.eea-inc.com/rrdb/DGRegProject/States/NE.html

Nevada

Nevada has an integrated program where both construction and operations are covered under the same permit.  Major sources are non-exempt sources that have a PTE of 250 tpy of any criteria pollutant or 50 tpy NOx or VOC in nonattainment areas, or 10 tpy or more of a HAP or 25 tpy or more of a combination of HAP.  Minor sources are sources that are not major sources.  Trivial activities (e.g., consumer use of paper trimmers/binders, equipment used to mix and packages soaps) and insignificant activities (e.g., crematory incinerators processing less than 175 tpy, autoclave rebricking) are provided.  Trivial activities are activities and emission units that may be presumptively omitted from Class I applications.  Insignificant activities are activities that are not subject to permitting in accordance with NAC 445B.288.4.  Sources that are not specifically exempted must obtain a minor source permit.  Subject minor sources are subject to BACT.

Sources:	http://ndep.nv.gov/bapc/qa/getting.html

http://www.eea-inc.com/rrdb/DGRegProject/States/NV.html

New Mexico

New Mexico State regulations governing NSR preconstruction permitting can be found at Title 20 (Environmental Protection), Chapter 2 (Air Quality (Statewide)), Part 72 (Construction Permits).  Regulations do not specifically define “minor” sources.  However, permits must be obtained for any new or modified stationary source that has a PTE greater than 10 lbs/hr or

25 tpy of any regulated air contaminant for which there is a National or State ambient air quality standard.

Emissions from a list of specified activities are not required (e.g., activities that occur strictly for maintenance of grounds or buildings, including: lawn care, pest control, grinding, cutting, welding, painting, woodworking, sweeping, general repairs, janitorial activities, and building rood operations) to be included in the calculation of the facility-wide potential emission rate. (NMAC 20.2.72.202)

If a source has a PTE less than 10 tpy of each criteria pollutant, the source is exempt from permitting.  No State notification is required.  If a source has a PTE between 10 to 25 tpy or

10 lb/hr of any criteria pollutant, a minor source permit is required.  In most cases, an air dispersion modeling analysis demonstrating compliance with applicable ambient standards needs to be submitted with the application.  The State ambient 24-hour NOx standard is more stringent than Federal standards, but there is no State BACT.  Controls may be necessary in areas where there are other NOx-emitting sources.

The presence of a specified list of sources/units and activities for which emissions do not need to be calculated (e.g., specified stand-by generators) at the facility shall be reported, as provided in the permit application forms.  Emissions from these sources and activities, however, are not required to be included in the calculation of the facility-wide potential emission rate.

The Department may, after notice and a public hearing with opportunity for public participations, issue one or more general construction permits, each covering numerous similar sources.

Sources:	Title 20, Environmental Protection, Chapter 2, Air Quality (Statewide), Part 72, Construction Permits.  20.2.72 NMAC

http://www.eea-inc.com/rrdb/DGRegProject/States/NM.html

North Dakota

A “minor source” is defined as any designated air contaminant source identified under NDAC 33-15-14-01 which is not required to obtain a Title V permit to operate under NDAC 33-15-14-06.  The process begins with obtaining a preconstruction permit.  Some units are exempt (e.g., bench scale laboratory equipment used exclusively for chemical or physical analysis or experimentation) from permitting under NDAC 33-15-14-13.  In such cases, no State notification is required, but is strongly recommended.  The department may require that the owner or operator of any stationary source exempted under subsection 13 to register the source.

The source must show that there would not be an exceedance of the NAAQS and PSD increments, which may require modeling, particularly if the source’s PTE is over 40 tpy of NOx or SO2 or 100 tpy of CO.

Source:	NDAC 33-15-14-01 to 33-15-14-07.  Designated Air Contaminant Sources, Permit to Construct, Minor Source Permit to Operate, Title V Permit to Operate.

Oklahoma

Oklahoma’s air regulations are promulgated under the Oklahoma CAA.  Oklahoma requires a preconstruction permit form the Air Quality Division when there is an addition of a new source, or modification of an existing source that results in a net increase in air contaminant emissions, as deemed necessary.  A minor source is any source for which a permit is required, but is not a Part 70 source.  Minor sources are either Group I sources, or Group II sources.  Group I sources emit at least 25 tpy, but less than 100 tpy of any one pollutant.  Group II sources emit more than 1 lb/hr but less than 25 tpy of any pollutant.

There are three permit categories: (1) permit by rule; (2) general permit; and (3) individual permit.

(1)  Permit by rule.  An owner or operator of a minor facility may apply for registration under a permit by rule if the following criteria are met:

(A)  The facility has actual emissions less than 40 tpy of each regulated air pollutant, except HAPs.

(B)  The facility does not emit or have the PTE 10 tpy or more of any single HAP or 25 tpy or more of any combination of HAPs.

(C)  The DEQ has established a permit by rule for the industry in Part 9 of this Subchapter.

(D)  The facility certifies that it will comply with the applicable permit by rule.

(E)  The facility is not operated in conjunction with another facility or source that is subject to air quality permitting.

(2)  General permit. Minor facilities may qualify for authorization under a general permit if the following criteria are met:

(A)  The facility has actual emissions less than 100 tpy of each regulated air pollutant, except for HAPs.

(B)  The facility does not emit or have the potential to emit 10 tpy or more of any single HAP or 25 tpy or more of any combination of HAPs.

(C)  The DEQ has issued a general permit for the industry.

(3)  Individual permit.  Minor facilities requiring permits which do not qualify for a permit by rule or a general permit shall obtain individual permits. An owner or operator may apply for an individual permit even if the facility qualifies for a permit by rule or a general permit.

There are three exemption conditions:  (1) A construction permit is not required for a minor source that releases less than or equal to 1 lb/hr for any criteria pollutant, and emits less than 100 tpy; (2) emissions of toxics do not exceed specified levels; and (3) the source/modification is not subject to a NESHAP or NSPS.  Oklahoma also specifies unit/source exemptions (e.g., for organic materials with vapor pressures of less than 1.5 psia under actual storage conditions, fugitive dust from agricultural sources).

Sources:	http://www.deq.state.ok.us/rules/100.pdf

Title 252.  Oklahoma Department of Environmental Quality.  Chapter 100.  Air Pollution Control.  Part 3 – Construction Permits.

Oregon

Air Contaminant Discharge Permits (ACDPs) are primarily used to regulate minor sources of air contaminant emissions, but are also required for any new major source or major modification of a major source.

There are six types of ACDPs (short term activity, basic, general, simple, standard, construction).  A General ACDP differs from other ACDPs in that general ACDPs are issued for an entire source category, and qualifying facilities are subsequently assigned to the permit.  The other types of ACDPs are issued for each individual facility.

For a long list of activities and sources (over 100) that constitute minor sources that require permits are specified in Table 1, OAR 340-216-0020.  Examples of sources on this list include autobody repair and painting shops painting more than 25 automobiles in a year; bakeries, commercial baking more than 500 tons of dough a year, etc.

General ACDPs are available for 18 source categories (e.g., hard chrome electroplaters, dry cleaners, asphalt plants).

Minor sources are sources that have the potential to emit less than major source thresholds.

Source:	http://www.deq.state.or.us/aq/aqpermit/ACDP/index.htm

South Dakota

Under the South Dakota’s Department of Environment and Natural Resources’ air regulations (Section 74:36), a minor source” is a source whose potential emissions of any regulated pollutant are less than 100 tpy and does not meet the definition of a Part 70 “major source.”   The State requires a preconstruction permit before any source or unit likely to cause the emission of air pollutants is constructed or modified.

Facilities that have a PTE less than 25 tpy of any criteria pollutant (except Pb) before control are exempt from permitting.  A letter of notification is required.  A single unit with a PTE less than 2 tpy is also exempt from permitting.  A source that has a PTE more than 25 tpy of any single criteria pollutant or actually emits more than 20 tpy of any criteria pollutant must obtain a minor source permit.  South Dakota’s regulations also include a list of source/unit exemptions (e.g., a device or apparatus fueled by waste oil, laboratory equipment used exclusively for chemical and physical analysis).

Sources for which General Permits have been developed include asphalt plants, rock crushers, concrete plants and grain elevators.  General permits can be obtained by submitting an application and the appropriate notice of intent to operate.

Sources:	http://www.eea-inc.com/rrdb/DGRegProject/States/SD.html

http://www.state.sd.us/denr/DES/AirQuality/airprogr.htm

Texas

Texas Administrative Code (TAC) rules permit both minor and major sources under the same requirements.  Any construction or modification of an existing facility which may emit air contaminants must comply with the following:

(1) obtain a permit,

(2) satisfy the conditions for a standard permit,

(3) satisfy the conditions for a flexible permit, or

(4) satisfy the conditions for exempt facilities.

Texas exempts specific facilities or types of facilities (called de minimis facilities or sources) that they have determined do not make a significant contribution of air contaminants to the atmosphere.  Texas’s exemption list includes over a 100 sources (e.g., music and film studios, farm and ranch refueling operations, offices, beauty shops).  For listed de minimis facilities or sources, neither registration or authorization prior to construction is required per Title 30 TAC Chapter 116.

Sources: http://www.tceq.state.tx.us/permitting/air/guidance/newsourcereview/demlist06_1377074.pdf

Utah

Utah State regulations governing NSR permitting are located in Rule 307-1-3, Control of Installations.

Exemptions and special provisions are specified in Rule 307-413.  Small source exemptions based on de minimis emissions are specified in Rule 307-413-2.  Sources with a actual emissions less than 5 tpy of any criteria pollutant or 500 lbs/yr of a HAP/air contaminant and less than 2,000 lbs/yr of any combination of HAP/air contaminant are exempt from permitting.

Other source exemptions are specified in Rule 307-413-4 (e.g., comfort heating equipment, exhaust systems for controlling steam and heat that do not contain combustion products).

Any project that does not meet exemption criteria and does not trigger Title V is subject to minor source permitting.  In the nonattainment areas of the state, offsetting and controls are likely.  State BACT is required in nonattainment area for NOx, PM, and SO2.  If emissions from a source are close to the major source threshold (250 tpy of any criteria pollutant in attainment areas, 100 tpy of any criteria pollutant in nonattainment or maintenance areas), it may be required to complete some modeling to determine the impact on the ambient air.  LAER may be required, depending on the modeling results.

Sources:	http://www.code-co.com/utah/admin/2000/r307413.htm

http://www.eea-inc.com/rrdb/DGRegProject/States/UT.html

Virginia

Minor NSR permits are issued to facilities that are large enough to emit pollutants above minimum “exemption” levels but do not qualify as “major” sources of air pollutants.  The Virginia minor NSR regulations require that a facility submit an application containing information about the facility before DEQ can issue a permit to the facility.  All applications are available for review by the public at the appropriate regional office.  Within Minor NSR permitting there is a subset of applications that include facilities that could be considered major stationary sources but have requested that the permit limit the amount of pollutants they can emit into the air (referred to as “synthetic minors”).

Any person or entity intending to construct a new air pollution source, or to modify, relocate or reactivate an existing source not exempt by 9 VAC 5-80-11 must apply for a minor new, modified, and certain major source construction permits.

Permit exemptions needs to be documented in writing from the appropriate DEQ regional office.  Specified facilities (e.g., vehicle refinishing operations, coating operations for the exterior of fully assembled aircraft or marine vessels) are exempt from construction, modification, reconstruction, or relocation provisions.  Virginia also specifies threshold-based exemptions.  Stationary sources with a PTE at rates less than all of the emission rates specified below shall be exempt from provisions pertaining to construction or relocation.

- 100 tpy of CO;

- 40 tpy of NOx;

- 40 tpy of SO2;

- 25 tpy of PM;

- 15 tpy of PM10;

- 25 tpy of VOC;

- 0.6 tpy of Pb;

- 3 tpy of fluorides;

- 6 tpy of sulfuric acid mist;

- 9 tpy of total reduced sulfur;

- 9 tpy reduced sulfur compounds;

- 3.6 x 10-6 tpy municipal waste combustor organics;

- 13 tpy municipal waste combustor metals;

- 35 tpy municipal waste combustor acid gases; and

- 22 tpy municipal solid waste landfill emissions (measured as NMOC).

The exemption of modified and reconstructed sources shall be determined as specified below.

Stationary sources with net emission increases less than all of the emission rates specified below shall be exempt from the modification or reconstruction provisions:

- 100 tpy of CO;

- 10 tpy of NOx;

- 10 tpy of S02;

- 15 tpy of PM;

- 10 tpy of PM10;

- 10 tpy of VOC;

- 0.6 tpy of Pb;

- 3 tpy of fluoride;

- 6 tpy of sulfuric acid mist;

- 9 tpy of total reduced sulfur;

- 3.5 x 10-6 tpy of municipal waste combustor organics;

- 13 tpy of municipal waste combustor metals;

- 35 tpy municipal waste combustor acid gases; and

- 22 tpy of municipal solid waste landfill emissions (measured as NMOC).

Exemptions from permitting do not stand for facilities subject to NSPS/NESHAP.

Source:	http://leg1.state.va.us/cgi-bin/legp504.exe

Washington

Washington regulations make no distinction between major and minor sources with regards to construction permits.  An air quality notice of construction (NOC) permit is required for a new source, or modification of an existing source if it emits air contaminants.  The notice must include a detailed description of the project, and include process equipment information, type and amount of air contaminants that would be emitted, air pollution control practices, and air pollution control equipment.

Sources with a PTE less than the thresholds listed below are exempt from permitting:

- PM10: 1.25 tpy

- NOx, SO2, and VOCs: 2 tpy

- CO: 5 tpy

- Pb: 0.005 tpy, and

- Ozone depleting substances: 1 tpy. (WAC 173-400-110(5))

Additionally, Washington exempts a long list of sources under WAC 173-400-110(4) (e.g., cleaning and sweeping of streets and paved surfaces; concrete application and installation).

A state BACT analysis for the appropriate pollutant is required for all minor sources with a PTE more than the de minimis levels listed above.  However, sources may take permit limits to avoid BACT.

Sources:

http://www.leg.wa.gov/wac/index.cfm?fuseaction=Section&Section=173-400-110

http://www.ecy.wa.gov/programs/air/airhome.html

http://www.eea-inc.com/rrdb/DGRegProject/States/WA.html

Wisconsin

Wisconsin defines a “minor source as “any facility, stationary source in an attainment area that emits less than 100 tpy of any criteria pollutant, less than 10 tpy of any individual federal HAP, and less than 25 tpy of all federal HAP combined.

Sources that are not exempt must obtain a minor permit.

Direct sources exempt from construction permit requirements are specified in NR 406.04 (e.g., storage tanks containing organic compounds with specified vapor pressures, portland concrete batch plants with production limits, graphic arts operations).

In order to be eligible for a specific exemption, the owner or operator of the source meet specified conditions (e.g., maintain records of materials used, emissions or production rates, must meet maximum theoretical emission thresholds).  Maximum theoretical emission thresholds include the following:

CO, SO2		< 9 lbs/hour each contaminant

PM, NOx, VOC	< 5.7 lbs/hour each contaminant

PM10			< 3.4 lbs/hour

Pb			< 0.13 lbs/hour

Sources:	http://www.dnr.state.wi.us/org/aw/air/

http://www.dnr.state.wi.us/org/aw/air/permitting

http://www.eea-inc.com/rrdb/DGRegProject/States/WI.html

Wyoming

Wyoming regulations governing minor source permitting can be found in Section 21 of the Wyoming Air Quality Act, Permit requirements for construction, modification, and operation.  There are no fixed exemption limits (de minimis thresholds), and the regulations do not explicitly define a minor source.  All sources are required to obtain a construction permit, unless the source/unit is specifically exempted (e.g., gasoline storage tanks at retail establishments, air conditioning or ventilating systems not designed to remove air pollutants generated by or released from equipment).  See Section 2(k) of Chapter 6 Wyoming Air Quality Standards and Regulations.  The State does have the ability to waive requirements based on impacts and emission rates on a case-by-case basis.  Based on a letter of intent sent to the regulatory agency, a source may be able to obtain an exemption.  Based on this application, the State will determine if BACT is necessary.

Regulations require facilities to utilize BACT to reduce or eliminate their emissions with consideration of technical practicability and economic reasonableness.

Sources:	http://deq.state.wy.us/

Wyoming Air Quality Standards and Regulations.  Chapter 6 – Permitting Requirements

http://www.eea-inc.com/rrdb/DGRegProject/States/WY.html

5.0  	Reference

Midwest Research Institute (MRI), 1997.  Review of State and Local Agencies’ New Source Preconstruction Permit Programs for Minor Sources.  Final Report.  Prepared for the U.S. Environmental Protection Agency, Information Transfer and Program Integration Division.  Office of Air Quality Planning and Standards.  Research Triangle Park, NC.  27711