MSFC PRACA : 2003-02-12 07:54

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A02312 | In-Flight Anomaly Number -- | Contractor Report Number E-045 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LO2 ULLAGE TRANSDUCER HAS CRACKED GLASS INSULATOR |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl Y | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE L02 ULL PRES TRNSDCR | PART# PD7400098-029 | SER/LOT# N/A | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion -- | F / U UC | Fail Mode -- | Cause -- |
| System ELECTRICAL | Defect -- | Material -- | Work Contact S. BRAGG | Fail Date 11/03/1980 |
| Received at MSFC 12/12/1980 | Date Isolated -- | FMEA Reference 3.1.1.9 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom -- | Time Cycle -- |
| Effectivity Text STS-1 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 07/15/1981 | Defer Date -- | Add Date -- | R/C Codes 1 - DES -- -- |
| Assignee |
| Design L. GUZINSKY | Chief Engineer -- | S & MA D. NEWMAN | Project R. ABRAHAM | Project MGR -- |
| Approval |
| Design L. GUZINSKY | Chief Engineer -- | S & MA D. NEWMAN | Project R. ABRAHAM | Project MGR -- |
| PAC Assignee C. NEWTON | PAC Review Complete CN | MSFC Closure Date 07/31/1981 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: MARS T35766 ON 9-13-80, GULTON, SCD, INITIATED MARS T-35766 STATING 23 WIPER ASSEMBLIES (P/N 121-718) USED IN THE BUILD OF LO2 ULLAGE TRANSDUCERS HAD CRACKS IN THE GLASS INSULATORS. RELIABILITY ASSURANCE INVESTIGATION CONFIRMED THE CONDITION & THAT THIS CONDITION WAS SUSPECT ON ALL DELIVERED LO2 ULLAGE TRANSDUCERS |
| Contractor Investigation/Resolution CAUSE - PROBABLE CAUSE IS VENDOR MANUFACTURING PROCESS. DETAILED INVESTIGATION IS IN PROCESS. INVESTIGATION - IT CAN BE ASSUMED THE PROBABILITY IS VERY HIGH, THAT THE WIPER ASSY GLASS BEAD INSULATORS (GULTON SCD P/N 121-726) ARE CRACKED ON UNITS INSTALLED ON ET-1 FURTHERMORE, BASED ON THE INSPECTION OF A 10% SAMPLE, ALL OF WHICH WERE CRACKED, ALL ASSYS MANUFACTURED TO DATE ARE ASSUMED TO BE DEFECTIVE ET-1 CONSTRAINT - CHANGES FROM STS-1 TO STS-2 WITH RATIONALE AS FOLLOWS: A) TO DATE, NO INSTANCES OF TRANSDUCER FAILURE HAVE BEEN ATTRIBUTED TO CRACKED GLASS INSULATORS. B) THE INSTALLATION OF SHOCK MOUNTED BRACKETS, WHICH DECREASES THE VIBRATION ENVIRONMENT (-12DB), REDUCES THE PROBABILTY OF ANY DEBRIS BEING DISLODGED. C) ONE UNIT KNOWN TO HAVE GLASS FRACTURES WAS TESTED AT THE VENDOR'S FACILITY. THE UNIT WAS MICRO- SCOPICALLY INSPECTED, SUBJECTED TO A O DEG F COLD SOAK & THEN VIBRATED AT ATP LEVELS. POST TESTING INSPECTION SHOWED NO FURTHER DEGRADATION OF THE CRACKS. D) A QUALIFICATION TEST UNIT (S/N 114) WAS OPENED & INSPECTED. THE GLASS BEAD WAS CRACKED. THIS WAS THE "WORST CASE" DEFECT OF ALL THE ASSYS INSPECTED. THIS UNIT HAD UNDERGONE THE VENDOR ATP PRECONDITIONING ON THE MPTA, QUAL & CONFIDENCE TESTING. THE UNIT WAS OPERATING & SERVICEABLE BEFORE DISASSEMBLY. E) THE TRANSDUCERS INSTALLED ON ET-1 ARE FUNCTIONING NORMALLY. THEY WILL BE CLOSELY MONITORED DURING FRF. F) THERE ARE FOUR TRANSDUCERS INSTALLED ON ET-1, 3 ACTIVE & 1 SPARE. EACH TRANSDUCER OPERATES A SEPARATE PRESSURIZATION CONTROL VALVE. THE SPARE GIVES THE LO2 TANK A MEASURE OF REDUNDANCY IN EVENT OF A TRANSDUCER FAILURE OF ANY TYPE PRIOR TO LIFTOFF. AFTER LIFTOFF, SHOULD A TRANSDUCER FAIL, THE TWO REMAINING TRANSDUCERS WOULD PROVIDE ADEQUATE TANK PRESSURIZATION CONTROL. 7/17/81 - RESOLUTION - ET-1: CONSTRAINT WAS REMOVED ON BASIS OF RATIONALE STATED IN TASK II OF CAPS (NO TRANSDUCER FAILURE HAS BEEN ATTRIBUTED TO CRACKED GLASS INSULATOR ANOMALLY). ET-2 AND SUBS: CONSTRAINT WAS REMOVED BASED ON REDESIGN OF TRANSDUCER TO INCLUDE POTTING THE GLASS INSULATOR NOW DESIGNATED PD7400098-079. ALSO THE VENDOR HAS AGREED TO IMPLEMENT MICROSCOPIC INSPECTION AND PULL TEST PRIOR TO POTTING OPERATION. DELTA QUALIFICATION TESTING HAS BEEN SUCCESS- FULLY PERFORMED ON THE REDESIGNED PRESSURE TRANSDUCER. NOTE: TASK VII OF CAPS E-045B HAS BEEN TRANSFERRED TO CAPS E-048C FOR TRACKING. 7/21/81 - CLOSURE DISTRIBUTED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A02312 | IFA# -- | Contractor RPT# E-045 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# -- | Asmnt Part Name -- | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD -- | CAUSE CD -- | FAIL MODE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |