DROUGHT MONITORING TASK FORCE

Drought Status Report

October 21, 2002

The Department of Environmental Quality compiled the following drought status report from information provided by the State Climatologist, the Virginia Departments of Agriculture and Consumer Services, Health, Forestry, Emergency Management, Game and Inland Fisheries; the Virginia Cooperative Extension Service, Farm Service Agency-USDA, the National Weather Service, and the U. S. Geological Survey.

## OVERVIEW

Drought conditions improved significantly throughout the Commonwealth due to rainfall since September 1.  The majority of the Commonwealth is currently experiencing moderate to extreme drought conditions.   Statewide rainfall for the first half of the month of October was 158% of long term average rainfall for this period.  Rainfall for the same period was above average in each of the Commonwealth’s climatic divisions.   Rainfall during the last six weeks (since September 1) was above long term average in all climatic divisions except the western Piedmont.  The long-range climatological outlook calls for equal chances of below average, average, and above average precipitation through January 2003.  Most streamgages across the Commonwealth recorded peak flows near bank full due to recent rainfall, with streamflows declining into the normal range of flow.  A few streamgages on larger rivers have recorded lower increases in streamflow.  With the onset of cooler temperatures and lower evapotranspiration demands these streamflows will not decline as rapidly as they have in the recent past.  Ground water levels have showed little improvements from the recent precipitation.  Levels of large reservoirs such as Lake Moomaw, Smith Mountain Lake, Kerr Reservoir, and Philpott Reservoir have begun to stabilize or improve due to variances to required minimum discharges and recent rainfall.  Normal to above normal rainfall since September 1 has improved hay and pasture conditions and has provided adequate soil moisture to support fall grain planting.  Ninety-one requests for agricultural drought designation have been received from seventy-seven separate localities.  Short term wildfire threats have significantly decreased due to increased forest fuel moisture.   These short term improvements do not eliminate the potential for an extreme fall wildfire season.   Reservoir and stream levels that support public water supplies have improved since the last report.   Ground water based public water supplies west of Route 95 have reported dropping ground water levels or reduced yields.  The Virginia Department of Health issued over 4000 private well replacement permits for private water supply wells that have failed during July and August.  Water conservation savings at large public water supplies continue to be reported since the implementation of the Governor’s Executive Order #33 on August 30.  The Department of Environmental Quality met with large users on the Roanoke River twice during October to continue discussions regarding allocating the limited flow in this river.  These discussions were initiated based on authority granted in Executive Order #33.  The cooler temperatures combined with recent rainfall have significantly improved conditions at the Department of Game and Inland Fishery’s hatcheries and allowed the stocking of trout as scheduled.    Most public boat ramps and fishing piers have increased accessibility when compared to one month ago but 19 boat ramps are out of service due to low levels.

CLIMATOLOGICAL CONDITIONS

#### National Weather Service

Remnants of tropical systems Hanna, Isidore and Kyle brought much needed precipitation to Virginia during the last thirty days.  Western and Southeastern Virginia received significant amounts of rainfall.  Rainfall totals over the last month were in excess of 5 inches in many locations, with several locations reporting amounts between 11 and 15 inches.  The city of Norfolk received well over 5 inches of rain from Isidore and over 3 inches from Kyle.  In addition, much of the Commonwealth received between 1 and 3 inches of rainfall during the last week.

The recent rainfall has provided significant short-term relief to the current drought situation.  However the long term conditions continue to be a concern.  Ground water has shown little response to recent rain and additional periodic and consistent rain throughout the fall and winter months are essential for overall improvement.

Over the next 7 to 14 days temperatures will be average to below average, with several opportunities for precipitation. The first chance for rain will occur from late October 19 into October 21, as a cold front stalls across the region. The potential exists for widespread one-half inch rainfall amounts from this system.  Cool Canadian high pressure will build into the Commonwealth from late October 21 through October  25, bringing the coldest weather so far this fall, as well as the possibility of widespread frost west of Route 95. A second chance for showers exists October 25, with a better chance for widespread precipitation on October 28-29.  A fourth chance of rain is currently forecast around Halloween.  Overall, the weather pattern for the next 2 weeks is favorable for periodic rainfall.  The amount of rainfall expected from these systems is unknown, but continued slow improvement in the overall drought situation appears likely.

The 30-day outlook through the month of November 2002 calls for equal chances of below average, average, and above average precipitation and temperatures.

The 90-day outlook through the month of January 2002 calls for equal chances of below average, average, and above average precipitation and temperatures.

The latest NOAA drought monitor indicates a significant improvement in drought conditions since the last report on September 19.  The drought monitor now indicates the majority of the Commonwealth is covered by moderate to extreme drought and is included as Appendix A.  Appendix B contains information from the national drought monitor with only Virginia displayed.  The NOAA seasonal drought outlook through January 2003 calls for improvement in drought conditions throughout the Commonwealth.  The seasonal drought outlook is included as Appendix C.

#### Report of the State Climatologist

Atmospheric circulation patterns have changed markedly since September 19 and now resemble a winter configuration that is conducive to below normal temperatures and more frequent precipitation.  As a result, statewide rainfall has been considerably above average (158% of normal) since October 1, with every climatic division in the state above average.

Since September 1, rainfall has also been above average over most of the state, although the Piedmont is generally near long-term historic mean precipitation. The Shenandoah Valley has received approximately 125% of normal rain since September 1.

As a result of this recent rainfall forest-fire related problems have diminished, and short-term crop conditions, including pasture growth and germination of winter crops have improved dramatically.  Other farm operations dependent upon standing water, such as livestock watering, remain precarious because there has yet to be a detectable increase in pond levels, with most in the Shenandoah Valley and many on the western Piedmont completely dry.

These very low pond levels are indicative of the long-term nature of the current drought.  Substantial rains associated with the remnants of Tropical Storm Isidore in late September produced little, if any, rise in many urban reservoirs, particularly in the highly stressed Charlottesville system.  This indicates extremely low deep soil moisture levels.  More recent precipitation has resulted in deep soil saturation and reservoir levels are beginning to rise.  It is very likely that the annual low values were observed on or near October 10, and that levels in general should rise for several months, absent a complete collapse in the current rainfall-producing mechanism.

A persistent pattern of high-pressure systems has developed in eastern Canada and New England.  This pattern tends to be very conducive to general rainfall in our region when low-pressure systems develop along the southern margin of this high.  Often these become substantial coastal cyclones (“northeasters”) which produce a general rain.  While medium and long-range forecast models do not accurately predict these events, they have the potential to provide significant drought relief to large areas of the Commonwealth.  In addition, this pattern tends to be associated with below normal temperatures which reduce evaporation and result in more efficient surface water recharge.

While current conditions indicate that most surface water systems will recharge, water conservation measures may still be required for some time.  For example, it is possible to recharge many systems with below-normal rain; but, the result will be systems that are full at the end of winter, embedded in an environment of below-normal streamflow and ground water.  These systems will then decline very rapidly during any subsequent dry conditions next spring/summer.  It is important to continue the water conservation message until we see the magnitude of winter rain and snow and its effects on current ground water levels and streamflows.

Appendix D contains tables of climatological division precipitation for various periods, from monthly, back to three years.

PROVISIONAL ASSESSMENT OF HYDROLOGIC CONDITIONS IN VIRGINIA

#### United States Geological Survey

Precipitation on October 15-16 resulted in 1-4 inches of rain across the Commonwealth.  Most streamgages recorded peak flows near bank full, with streamflows declining into the normal range of flow.  A few streamgages on larger rivers have recorded lower increases in streamflow.  Streamflow at the James River at Cartersville, Va., and the Roanoke River at Randolph, Va., have increased only to the lower range of normal flow.

The substantial amount of precipitation over the entire Commonwealth and the relatively low intensity of the rainfall should help relieve both shallow and deep soil moisture deficits.  The resulting higher soil moisture should increase ground-water recharge associated with future precipitation events this fall and winter.  Streamflow recession following the peak flows should not be as steep as the previous recessions last summer, and streamflows should be sustained slightly longer as a result of reduced evaporation and transpiration.

Appendix E contains flow duration and current flow conditions for selected U.S. Geological Survey and Virginia Department of Environmental Quality surface-water gaging stations.  Data are provisional and subject to revision.  The normal range of flows is defined as flows in the middle two quartiles (between those flows equaled or exceeded 75 percent of the time and those flows equaled or exceeded 25 percent of the time).

#### Department of Environmental Quality, Status of Major Reservoirs

In general, recent rains have reduced or reversed the declines in most major reservoirs, boding well for the prospects of refilling these sources of supply over the coming winter.  Lake Philpott is an exception.

Smith Mountain Lake has stabilized at 3.88 feet below full.  The lake continues to operate under a release variance.  The current release varies between 300 and 350 cfs compared to a normal release of 650 cfs.  Less water is released when runoff from storms result in increased levels of sideflow downstream of the dam.  This practice accelerates lake refilling without harming the Roanoke River.

Heavy rain in North Carolina has raised Kerr Reservoir to 295.3 feet above mean sea level, up 2 feet from September.  Current releases are 2200 cfs and will remain at this level.  The reservoir is filling.  Inflows are 7000 cfs two days after the rainfall on October 15th and 16th.

The elevation of Philpott Reservoir is 963.7; about the same as last report.  Minimum releases have been cut back to one fourth of their normal condition.

Lake Moomaw in western Virginia has 31.5% of the conservation pool remaining and has been operating under reduced releases since August 23rd.  This is a reduction in storage of 3.5% from the last report.  Inflow is 370 cfs and outflow is 133 cfs.  Concerns regarding completely utilizing the conservation pool this fall have diminished significantly.

Lake Anna was 4.8 feet down at an elevation of 245.2 feet on October 14.  This lake level does not include any rain from the state-wide storm on October 15 and 16 which probably dropped about 2.0+ inches of rain on the watershed.  This is down only 0.2 feet from the last report.  Dominion Power now reports potential shutdown of the nuclear power station on Lake Anna will not occur until August of 2003.

Claytor Lake on the New River is about a foot below full and rising.  This lake level will be back to normal soon.

VIRGINIA AGRICULTURAL SITUATION

#### Virginia Department of Agriculture and Consumer Services

Local Disaster Designation Requests

Ninety-one requests for federal drought disaster designation have been submitted to the Governor.  This is up from seventy-three requests on September 16.  These requests are from seventy-seven separate counties with fourteen of the seventy-seven submitting a second request for additional damages experienced since their original requests.  The U.S. Secretary of Agriculture has approved primary disaster designation for 10 of the localities (Bedford, Brunswick, Buckingham, Cumberland, Fluvanna, Goochland, Louisa, Orange, Prince Edward, and Rockbridge counties) and has denied disaster designation for six localities (Augusta, Bland, Nelson, Page, Rockingham and Wythe counties) whose loss of production did not meet the 30% federal requirement.  The Governor has submitted sixty-nine requests for federal designation for sixty-seven other localities whose approval is still pending (Accomack, Albemarle, Amelia, Amherst, Appomattox, Augusta (2nd request), Bedford (2nd request), Bland (2nd request),  Botetourt, Buckingham (2nd request), Campbell, Campbell (2nd request),  Caroline, Carroll, Charles City,  Charlotte, Chesterfield, Craig, Culpeper, Cumberland (2nd request), Dinwiddie, Essex, Fauquier,  Floyd,  Franklin, Franklin (2nd request), Goochland (2nd request), Grayson, Greene, Greensville, Halifax, Hanover, Henrico, Henry, Isle of Wight, King and Queen, King George, King William, Lancaster, Lee, Louisa (2nd request), Lunenburg, Madison, Mecklenburg, Middlesex, Montgomery, Nelson (2nd request), New Kent, Nottoway, Page (2nd request), Patrick, Pittsylvania, Powhatan, Prince George, Prince William, Pulaski, Rappahannock, Richmond, Roanoke, Rockingham (2nd request), Russell, Scott, Spotsylvania, Stafford, Suffolk, Surry, Warren, Westmoreland and Wythe (2nd request) counties).   Damage assessment reports (DAR) are pending from USDA for six localities (Alleghany, Giles, Northampton, Northumberland, Orange (2nd request) and Shenandoah counties).   Thirty-eight different localities have received secondary designation because they are contiguous to counties that have primary designation.  In addition, eight localities who have received primary designation have also received secondary designation.

United States Secretary of Agriculture Veneman announced on September 19, 2002, that the United States Department of Agriculture was allocating $752 million for a Livestock Compensation Program that would provide immediate and direct disaster relief for qualifying American farmers in drought-impacted states. The Secretary also announced that this new program would be available only in localities named as primary disaster areas or that are covered by disaster designation requests submitted by a State Governor, no later than September 19, 2002, and are subsequently approved by the Secretary.  Forty-five Virginia localities could meet the eligibility requirements for the Livestock Compensation Program.  Approximately 30 other Virginia localities will not qualify based on this deadline for submission of disaster requests.

Crop Weather Summary

Virginia experienced cooler temperatures and welcomed rain. The rain greened up pastures and hay fields. This will provide for good fall grazing in some areas of the state if temperatures do not drop drastically over the next couple of weeks.  The rain received helped maintain topsoil moisture for small grain seeding.

Tables describing topsoil moisture, crop condition, and crop progress are contained in Appendix F.

FOREST SITUATION IN VIRGINIA

#### Virginia Department of Forestry

Wildfire Conditions

Several successive rain events have helped to end an above normal summer wildfire season, and will help to delay the start of the normal fall wildfire season here in the Commonwealth.  It is important to note that in spite of the rain, the fall wildfire season is not yet over.  Dry weather following leaf fall remains the biggest concern, and November is historically the most active month during the fall wildfire season (see Appendix G).  Recent rain has certainly helped to reduce the overall wildfire potential at this point; however more is needed in mid-November to really put an end to the threat for the fall.  The Commonwealth's official fall wildfire season runs from October 15 until November 30.

There has been a great deal of interest generated regarding the potential for closing the fall hunting seasons. This is always a sensitive issue that must balance the interests of numerous parties throughout the Commonwealth.  The State Forester and the Director of the Department of Game and Inland Fisheries remain in close contact regarding this issue.  It is always hazardous to predict what will happen regarding wildfire activity, because the weather can and does change so dramatically over a short period of time.  At this point, no steps have been taken to issue a forest closure or to close any part of hunting season.

Through October 15, the DOF has responded to 1,629 wildfires that burned 13,195 acres this calendar year. This activity remains well above the normal five and ten year averages.

### PUBLIC WATER SUPPLY SYSTEMS

#### Virginia Department of Health

Mandatory water restrictions are in place in most of the Commonwealth due to Executive Order #33.  Only southwest Virginia, parts of northern Virginia, and the Eastern Shore are not included in the order.

The Division of Drinking Water contacted community waterworks serving 10,000 or more customers and requested they provide a weekly report of the average daily water produced/purchased.  In addition, VDH staff prepared baseline data for these waterworks which included the average daily water production data for each month in calendar year 2001and for August 2002.  The data obtained requires a cautious interpretation as there are many external factors such as some waterworks have been on various degrees of conservation for some time, water production facilities can be taken off-line for certain periods of time, many systems are highly interconnected with multiple suppliers, an expected lag between conservation orders and results, etc.  An additional external factor that must be considered when examining these calculated conservation savings is the normal reduction in water demands as we move into the fall/winter season.

During the week of September 16 the data indicated an average conservation savings of 12.70% (71,671,974 gallons per day) occurred as compared to August 2002 (just prior to EO 33) and 9.65% (54,137,463 gallons per day) as compared to August 2001.  Data from the week of September 16 was also compared to reported withdrawals from September 2001.  This comparison indicated an average water conservation saving of 8.14% (43,032,110 gallons per day).

During the week of September 23 the data indicated an average conservation savings of 13.82% (81,968,297 gallons per day) occurred as compared to August 2002 (just prior to EO 33) and 10.92% (64,427,786 gallons per day) as compared to August 2001.  Data from the week of September 23 was also compared to reported withdrawals from September 2001.  This comparison indicated an average water conservation saving of 9.43% (53,328,433 gallons per day).  In each comparison, water conservation increased by approximately 10,000,000 gallons per day when compared to the week of September 16.

During the week of September 30 the data indicated an average conservation savings of 11.81% (62,933,577 gallons per day) occurred as compared to August 2002 (just prior to EO 33) and 7.39% (34,293,713 gallons per day) as compared to September 2001.  Data from the week of September 30 was also compared to reported withdrawals from October 2001.  This comparison indicated an average water conservation saving of 3.78% (15,182,911 gallons per day).

During the week of October 7 the data indicated an average conservation savings of 17.45% (93,841,348 gallons per day) occurred as compared to August 2002 (just prior to EO 33), 13.30% (65,214,911 gallons per day) as compared to September 2001and 9.97% (46,239,843 gallons per day) as compared to October 2001.

Significant rainfall occurred across much of the state in the last week.  Many surface water reservoirs are now reporting full conditions.  Others have received substantial inflow.  A total of 95 surface water systems are included in this report.  Only 13 report worsening conditions, with the remainder reporting better or same/stable conditions.

Ground water conditions continue to remain low west of Interstate 95.  Several water systems have lost wells and had new wells drilled or are having water hauled to their customers.  A total of 24 ground water systems are included in this report.  Only 2 report worsening conditions, with the remainder reporting better or same/stable conditions.

Several areas have reported both public and private wells are going dry.  County Health Departments from across the Commonwealth report the issuance of more than 4,000 replacement well permits during July and August 2002.

Appendix H contains detailed reports of public water supply conditions in the six field offices as reported on October 16.

Appendix I lists sixteen waterworks that appear to be on the verge of critical drought conditions.  The starting point for selecting the waterworks was the Drought Survey performed by the Division of Drinking Water in August, 2002.  The “watch status” has been further defined as those that may fail in the next 90 days (through January 15, 2002) without adequate rainfall.

The following criteria were applied in developing the list contained in Appendix I: 
A. From the survey database a sort was performed for waterworks that answered YES to question #6(Are you having drought related supply problems?) and YES to question #7(...do you expect to have problems over the next 90 days?) 
B. A comparison was then made to our latest weekly drought reports. 
C. Consecutive waterworks were not included. 
D. Generally, only those that reported that they were on Voluntary or Mandatory conservation were included. 
E. No alternative sources (of any kind) were available or would be available within 90 days. 
F. For Surface sources <= 90 days remaining in reservoirs (as applicable). 
G. For groundwater sources-critical (subjective) production or well water levels.

FISHERIES AND RECREATIONAL IMPACTS

#### Virginia Department of Game and Inland Fisheries

Stream and river levels are at or above average across the majority of the Commonwealth for the first time in several months.  As a result, canoe and small powerboat opportunities are available in many areas. Reservoir levels will require several more significant rainfall events to reach seasonal pool elevations.  At this time, 19 Department boat ramps at public reservoirs are closed due to low water.  Boaters are encouraged to check the Department’s web site (www.dgif.state.va.us) for ramp conditions.

Flow variances remain in effect for Leesville Reservoir (Roanoke River/Smith Mountain Lake), Lake Anna (North Anna River) Claytor Lake (New River) and Lake Moomaw (Jackson River).

The cooler temperatures combined with recent rainfall have significantly improved conditions at the Department’s hatcheries and allowed the stocking of trout as scheduled.  The probability of fish kills in ponds and lakes due to low oxygen has decreased significantly.

All hunting seasons are going forward as scheduled with campers being reminded that a few days of dry conditions can increase fire hazards significantly.

LOCAL EMERGENCY DELCARATIONS/REQUESTS FOR ASSISTANCE

Virginia Department of Emergency Management

The Towns of Orange, Gordonsville, and Gretna and Amherst County’s requests for reimbursement under the Commonwealth's Emergency Relief to Localities program have been denied.

##### APPENDIX A

National Drought Summary – October 15, 2002

The Mid-Atlantic and Southeast: After missing out on the bulk of remnant hurricane rainfall each of the past two weeks, most of the Atlantic Seaboard welcomed widespread beneficial rains this last week. From central Georgia up to Long Island, rainfall reports of 2 to 4 inch soakings were widespread. Rain was heaviest (6” +) off the southeast coast (and just inland) as the formerly stronger Kyle sat off the Carolina and Georgia coastlines. This rainfall helped to start eroding away at the drought along the coastal areas of Georgia, the Carolinas and Virginia. While the rains were not as heavy further inland (or on the western Appalachian front), they were good enough to remove the exceptional (D4) drought in the Carolinas and southern Virginia. They also led to the reduction of the core area of extreme (D3) drought in the same region. Accordingly, the D0 and D1 areas were also reduced and pushed inland off of their respective coasts.  Guarded optimism is the general rule here as overall improvement in the region this week is reflected by a general tightening and pushing (one category improvement) of the drought boundaries westward off the coastal stretches in the Carolinas and eastern Virginia. The rains brought a welcome reversal to an intensification pattern (dry) that was re-emerging in the region earlier this fall. While short-term numbers are positive, the region is still dealing with a drought of long-term proportions as year-to-date deficits still fall in the 6-12 inch range. Going back to October of 2001, we see many locations still facing deficits of 12-18 inches from southeast Georgia and east-central Alabama up through the Carolinas and into Virginia and Maryland. Fire danger has been reduced and top soil moisture conditions have improved considerably over the past few weeks leading to a removal of the “A” and “F” impact labels in the East. The recent rains have resulted in the region falling exclusively under the “W” (water/hydro) impact delineation. This signifies that while many areas have reduced their short-term deficits and resultant impacts, the long-term drought and its impacts will still persist unless this recent favorable wet trend continues over the coming weeks and months. Ground water levels remain at record lows at many locations and streamflow and reservoir levels need to continue to improve.

APPENDIX B

##### APPENDIX C

Latest Seasonal Assessment - Heavy and widespread rains during October have led to major drought improvement across the East, and the outlook calls for continued improvement in coming months. Long-term precipitation deficits continue despite the recent rains and, as a result, some wells and reservoirs may remain at lower-than-average levels into winter but, at this point, the mild, dry pattern that took hold a year ago does not seem to be repeating. Confidence for improvement is greatest in the Southeast, where the precipitation outlook for November through January calls for above-normal precipitation.

##### APPENDIX D

Precipitation departures by Climatological Division.

Two Week Precipitation Departures

| Climatological Division | OCT 1-16 | OCT 1-16 | OCT 1-16 | OCT 1-16 |
| --- | --- | --- | --- | --- |
|  | 2002 | NORMAL | DEPARTURE | % NORMAL |
| Tidewater | 3.30 | 1.68 | 1.62 | 197% |
| Eastern Piedmont | 3.30 | 1.71 | 1.59 | 193% |
| Western Piedmont | 2.30 | 1.83 | 0.47 | 126% |
| Northern | 2.60 | 1.79 | 0.81 | 145% |
| Central Mountain | 2.00 | 1.72 | 0.28 | 117% |
| Southwestern | 2.30 | 1.55 | 0.75 | 149% |
| Statewide | 2.70 | 1.71 | 0.99 | 158% |

Six Week Precipitation Departures

| Climatological Division | SEPT-OCT 16 | SEPT-OCT 16 | SEPT-OCT 16 | SEPT-OCT 16 |
| --- | --- | --- | --- | --- |
|  | 2002 | NORMAL | DEPARTURE | % NORMAL |
| Tidewater | 5.78 | 5.53 | 0.25 | 105% |
| Eastern Piedmont | 5.31 | 5.16 | 0.15 | 103% |
| Western Piedmont | 5.36 | 5.54 | -0.18 | 97% |
| Northern | 6.39 | 5.19 | 1.20 | 123% |
| Central Mountain | 6.23 | 4.87 | 1.36 | 128% |
| Southwestern | 6.13 | 4.63 | 1.50 | 132% |
| Statewide | 5.84 | 5.17 | 0.67 | 113% |

Ten Week Precipitation Departures

| Climatological Division | AUG-OCT 16 | AUG-OCT 16 | AUG-OCT 16 | AUG-OCT 16 |
| --- | --- | --- | --- | --- |
|  | 2002 | NORMAL | DEPARTURE | % NORMAL |
| Tidewater | 10.06 | 10.32 | -0.26 | 97% |
| Eastern Piedmont | 10.13 | 9.49 | 0.64 | 107% |
| Western Piedmont | 8.68 | 9.81 | -1.13 | 89% |
| Northern | 9.60 | 9.27 | 0.33 | 104% |
| Central Mountain | 7.78 | 8.82 | -1.04 | 88% |
| Southwestern | 8.51 | 8.56 | -0.05 | 99% |
| Statewide | 9.21 | 9.42 | -0.21 | 98% |

Fourteen Week Precipitation Departures

| Climatological Division | JULY-OCT 16 | JULY-OCT 16 | JULY-OCT 16 | JULY-OCT 16 |
| --- | --- | --- | --- | --- |
|  | 2002 | NORMAL | DEPARTURE | % NORMAL |
| Tidewater | 12.80 | 15.34 | -2.54 | 83% |
| Eastern Piedmont | 13.33 | 14.15 | -0.82 | 94% |
| Western Piedmont | 13.02 | 14.44 | -1.42 | 90% |
| Northern | 13.47 | 13.34 | 0.13 | 101% |
| Central Mountain | 12.54 | 12.84 | -0.30 | 98% |
| Southwestern | 13.31 | 13.11 | 0.20 | 102% |
| Statewide | 13.12 | 13.96 | -0.84 | 94% |

Thirty-eight Week Precipitation Departures

(Year to date)

| Climatological Division | JAN-OCT 16 | JAN-OCT 16 | JAN-OCT 16 | JAN-OCT 16 |
| --- | --- | --- | --- | --- |
|  | 2002 | NORMAL | DEPARTURE | % NORMAL |
| Tidewater | 32.07 | 36.33 | -4.26 | 88% |
| Eastern Piedmont | 29.55 | 35.45 | -5.90 | 83% |
| Western Piedmont | 29.01 | 36.74 | -7.73 | 79% |
| Northern | 30.51 | 33.25 | -2.74 | 92% |
| Central Mountain | 28.33 | 32.57 | -4.24 | 87% |
| Southwestern | 35.30 | 35.62 | -0.32 | 99% |
| Statewide | 30.99 | 35.23 | -4.24 | 88% |

One Year Precipitation Departures

| Climatological Division | NOV 2001- | NOV 2001- | NOV 2001- | NOV 2001- |
| --- | --- | --- | --- | --- |
|  | OCT 16, 2002 | OCT 16, 2002 NORMAL | OCT 16, 2002 DEPARTURE | OCT 16, 2002 % NORMAL |
| Tidewater | 34.26 | 42.26 | -8.00 | 81% |
| Eastern Piedmont | 32.11 | 41.56 | -9.45 | 77% |
| Western Piedmont | 32.31 | 42.94 | -10.63 | 75% |
| Northern | 33.15 | 39.06 | -5.91 | 85% |
| Central Mountain | 31.33 | 38.08 | -6.75 | 82% |
| Southwestern | 38.57 | 41.75 | -3.18 | 92% |
| Statewide | 33.82 | 41.19 | -7.37 | 82% |

Two Year Precipitation Departures

| Climatological Division | NOV 2000- | NOV 2000- | NOV 2000- | NOV 2000- |
| --- | --- | --- | --- | --- |
|  | OCT 16, 2002 | OCT 16, 2002 NORMAL | OCT 16, 2002 DEPARTURE | OCT 16, 2002 % NORMAL |
| Tidewater | 70.49 | 85.89 | -15.40 | 82% |
| Eastern Piedmont | 67.15 | 84.52 | -17.37 | 79% |
| Western Piedmont | 66.21 | 87.37 | -21.16 | 76% |
| Northern | 69.66 | 79.59 | -9.93 | 88% |
| Central Mountain | 63.19 | 77.56 | -14.37 | 81% |
| Southwestern | 78.70 | 84.78 | -6.08 | 93% |
| Statewide | 69.62 | 83.77 | -14.15 | 83% |

Three Year Precipitation Departures

| Climatological Division | NOV 1999- | NOV 1999- | NOV 1999- | NOV 1999- |
| --- | --- | --- | --- | --- |
|  | OCT 16, 2002 | OCT 16, 2002 NORMAL | OCT 16, 2002 DEPARTURE | OCT 16, 2002 % NORMAL |
| Tidewater | 117.24 | 129.52 | -12.28 | 91% |
| Eastern Piedmont | 106.75 | 127.48 | -20.73 | 84% |
| Western Piedmont | 105.53 | 131.80 | -26.27 | 80% |
| Northern | 107.69 | 120.12 | -12.43 | 90% |
| Central Mountain | 104.64 | 117.04 | -12.40 | 89% |
| Southwestern | 117.22 | 127.81 | -10.59 | 92% |
| Statewide | 110.33 | 126.35 | -16.02 | 87% |

APPENDIX E

Flow duration and current flow conditions for selected U.S. Geological Survey and Virginia Department of Environmental Quality surface-water gaging stations

|  | MINIMUM DAILY FLOW, PERIOD OF RECORD (CFS) | MINIMUM OCTOBER FLOW, PERIOD OF RECORD (CFS) | 7Q2 (CFS) | 7Q10 (CFS) | PERCENT OF TIME FLOW EQUALED OR EXCEEDED FOR OCTOBER DAILY MEAN FLOWS (CUBIC FEET PER SECOND) | CURRENT CONDITIONS FLOW (CFS)/ DURATION (PERCENT) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 75% | 50% | 25% | October 18, 2002 |
| SHENANDOAH RIVER BASIN |  |  |  |  |  |  |  |  |
| South River near Waynesboro, Va. | 17 | 22 | 30 | 24 | 33 | 42 | 84 | 27 |
| South Fork Shenandoah River at Front Royal, Va. | 107 | 118 | 344 | 235 | 385 | 517 | 855 | 467 |
| North Fork Shenandoah River at Cootes Store, Va. | 0.2 | 0.4 | 3.2 | 0.77 | 4.6 | 12 | 52 | 261 |
| North Fork Shenandoah River near Strasburg, Va. | 35 | 35 | - | - | 114 | 159 | 274 | 1,550 |
| POTOMAC RIVER BASIN |  |  |  |  |  |  |  |  |
| Goose Creek near Leesburg, Va. | 0.4 | 0.8 | 12 | 2.5 | 18 | 48 | 131 | - |
| RAPPAHANNOCK RIVER BASIN |  |  |  |  |  |  |  |  |
| Rappahannock River at Remington, Va. | 2.9 | 5.0 | 50 | 11 | 80 | 174 | 385 | 479 |
| Rapidan River near Culpeper, Va. | 2.2 | 2.2 | - | - | 90 | 160 | 367 | 236 |
| Rappahannock River near Fredericksburg, Va. | 5.0 | 5.0 | 189 | 48 | 227 | 449 | 925 | 2,070 |
| YORK RIVER BASIN |  |  |  |  |  |  |  |  |
| Pamunkey River near Hanover, Va.* | 45 | 18 | - | - | 115 | 215 | 442 | 220 |
| Mattaponi River near Beulahville, Va. | .78 | 8.3 | 48 | 14 | 66 | 154 | 319 | 66 |

|  | MINIMUM DAILY FLOW, PERIOD OF RECORD (CFS) | MINIMUM OCTOBER FLOW, PERIOD OF RECORD (CFS) | 7Q2 (CFS) | 7Q10 (CFS) | PERCENT OF TIME FLOW EQUALED OR EXCEEDED FOR OCTOBER DAILY MEAN FLOWS (CUBIC FEET PER SECOND) | CURRENT CONDITIONS FLOW (CFS)/ DURATION (PERCENT) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 75% | 50% | 25% | October 18, 2002 |
| JAMES RIVER BASIN |  |  |  |  |  |  |  |  |
| Jackson River near Bacova, Va. | 13 | 17 | 26 | 20 | 25 | 32 | 61 | 112 |
| Potts Creek near Covington, Va. | 15 | 16 | 24 | 17 | 29 | 38 | 69 | 72 |
| Cowpasture River near Clifton Forge, Va. | 40 | 42 | 73 | 54 | 86 | 110 | 193 | 584 |
| Craig Creek at Parr, Va. | 25 | 29 | 43 | 31 | 50 | 70 | 131 | 169 |
| James River at Buchanan, Va.* | 207 | 239 | 378 | 271 | 429 | 563 | 922 | 2,140 |
| Maury River near Buena Vista, Va. | 22 | 22 | 89 | 62 | 110 | 158 | 263 | 259 |
| Hardware River below Briery Run near Scottsville, Va | 0.1 | 4.8 | 24 | 7.5 | 28 | 45 | 80 | 40 |
| Rivanna River at Palmyra, Va. | 5.2 | 13 | - | - | 118 | 204 | 424 | 188 |
| James River at Cartersville, Va. | 330 | 348 | 1,120 | 584 | 1,380 | 2,000 | 3,600 | 1,520 |
| Appomattox River at Farmville, Va. | 6.3 | 6.3 | 52 | 21 | 67 | 105 | 162 | 198 |
| Appomattox River at Mattoax, Va. | 13 | 13 | 86 | 30 | 119 | 206 | 335 | 400 |
| Chickahominy River near Providence Forge, Va. | 0.07 | 0.07 | 16 | 4.0 | 22 | 60 | 172 | 117 |
| CHOWAN RIVER BASIN |  |  |  |  |  |  |  |  |
| Nottoway River near Sebrell, Va. | 14 | 14 | 82 | 24 | 82 | 217 | 609 | 448 |
| Blackwater River near Franklin, Va. | 0.07 | 0.07 | - | - | 7 | 54 | 305 | 78 |
| Meherrin River near Lawrenceville, Va. | 4.2 | 4.2 | 52 | 16 | 62 | 115 | 212 | 620 |

|  | MINIMUM DAILY FLOW, PERIOD OF RECORD (CFS) | MINIMUM OCTOBER FLOW, PERIOD OF RECORD (CFS) | 7Q2 (CFS) | 7Q10 (CFS) | PERCENT OF TIME FLOW EQUALED OR EXCEEDED FOR OCTOBER DAILY MEAN FLOWS (CUBIC FEET PER SECOND) | CURRENT CONDITIONS FLOW (CFS)/ DURATION (PERCENT) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | 75% | 50% | 25% | October 18, 2002 |
| ROANOKE RIVER BASIN |  |  |  |  |  |  |  |  |
| Roanoke River at Roanoke, Va.* | 19 | 30 | 58 | 35 | 77 | 107 | 186 | 103 |
| Pigg River near Sandy Level, Va. | 25 | 51 | 96 | 47 | 136 | 175 | 266 | 266 |
| Roanoke River at Randolph, Va.* | 179 | 282 | 847 | 426 | 1,020 | 1,310 | 1,980 | 1,000 |
| Dan River at Paces, Va. | 244 | 280 | - | - | 912 | 1,200 | 1,780 | 3,390 |
| Hyco River near Denniston, Va.* | 1.5 | 0.3 | - | - | 18 | 33 | 62 | 435 |
| KANAWHA RIVER BASIN |  |  |  |  |  |  |  |  |
| New River at Allisonia, Va. | 453 | 534 | 1,040 | 725 | 1,060 | 1,520 | 2,330 | 3,510 |
| Little River at Graysontown, Va. | 47 | 59 | 109 | 69 | 133 | 180 | 275 | 229 |
| Walker Creek at Bane, Va. | 24 | 30 | 44 | 33 | 46 | 62 | 107 | 245 |
| BIG SANDY RIVER BASIN |  |  |  |  |  |  |  |  |
| Russell Fork at Haysi, Va. | 0.2 | 0.5 | 8.7 | 1.0 | 12 | 27 | 62 | 94 |
| TENNESSEE RIVER BASIN |  |  |  |  |  |  |  |  |
| South Fork Holston River near Damascus, Va. | 40 | 66 | 99 | 73 | 100 | 132 | 202 | 312 |
| North Fork Holston River near Saltville, Va. | 2.0 | 2.0 | 34 | 24 | 35 | 50 | 94 | 213 |
| Clinch River at Cleveland, Va. | 37 | 42 | 81 | 54 | 89 | 122 | 223 | 479 |
| Powell River near Jonesville, Va. | 18 | 18 | 42 | 24 | 46 | 68 | 126 | 146 |
| * indicates some regulation |  |  |  |  |  |  |  |  |

APPENDIX F

Virginia Agriculture Statistic Services report of topsoil moisture, crop condition and crop progress.

| TOPSOIL MOISTURE PERCENT |
| --- |
| Week Ending | Very Short | Short | Adequate | Surplus |
| October 13 | 13 | 35 | 50 | 2 |
| October 6 | 20 | 39 | 40 | 1 |
| September 29 | 20 | 29 | 48 | 3 |
| September 22 | 30 | 32 | 38 | 1 |

| CROP CONDITION PERCENT |
| --- |
| Crop | Very Poor | Poor | Fair | Good | Excellent |
| Pastures | 18 | 31 | 31 | 19 | 1 |
| Livestock | 1 | 16 | 35 | 43 | 4 |
| Other Hay | 19 | 29 | 32 | 19 | 1 |
| Alfalfa Hay | 11 | 18 | 37 | 33 | 1 |
| Soybeans | 18 | 34 | 32 | 13 | 3 |
| Peanuts | 13 | 28 | 26 | 30 | 3 |
| Cotton | 7 | 29 | 34 | 28 | 2 |
| Apples, All | 16 | 12 | 42 | 30 | 0 |

| CROP PROGRESS PERCENT – WITH COMPARISONS |
| --- |
| Crop | This Week | Last Week | Last Year | 5 Year Average |
| Corn Harvested for Grain | 82 | 71 | 70 | 64 |
| Soybeans Dropping Leaves | 77 | 60 | 80 | 62 |
| Soybeans Harvested | 15 | 8 | 12 | 9 |
| Winter Wheat Seeded | 18 | 13 | 20 | 14 |
| Barley Seeded | 59 | 34 | 42 | 36 |
| Flu Cured Tobacco Harvested | 78 | 69 | 100 | 93 |
| Peanuts Dug | 62 | 40 | 72 | 71 |
| Cotton Bolls Opening | 97 | 92 | 84 | 87 |
| Cotton Harvested | 39 | 27 | 27 | 22 |
| Fall Apples Harvested | 86 | 77 | 70 | 71 |
| Winter Apples Harvested | 49 | 40 | 47 | 43 |

##### APPENDIX G

##### APPENDIX H

Virginia Department of Health Field Office Reports for Public Water Systems (October 16, 2002)

(Note: The first digit in the PWSID number indicates the field office location of the waterworks.  PWSID 2770650 is located in the Lexington Field Office, etc.)

| PWSID 1-Abingdon 2-Lexington 3-Southeast VA 4-East Central 5-Danville 6-Culpeper | Waterworks | Source Name | Restrictions N: No M: Mandatory V: Voluntary | Situation B: Better, S: Same/Stable, W: Worse |
| --- | --- | --- | --- | --- |
| 2043629 | Keystone Baptist Church | Drilled Wells | V | W: Well yields down significantly. Well 1 yield has fallen from 8 gpm to 1.5 gpm. Well 2 has yield of 1.5 gpm. Combined yields have periodically not meet demand. Instituted use of bottled water and increased emphasis to students and faculty to minimize water use. Currently investigating installation of storage and water hauling options. Estimated student/staff population 90. |
| 2003725 | Charlottesville/Albemarle County | South Rivanna (South Rivanna WTP) | M | W: Their main reservoir-South Rivanna (South Rivanna WTP) is 4.2 feet below full. Overall source water availability is at 55.5% of "full available capacity" (this includes both the South Rivanna system and the Sugar Hollow/Ragged Mountain system). Water restrictions are in excess of EO-33. |
| 2003600 | Charlottesville/Albemarle County | Sugar Hollow and Ragged Mountain Reservoirs (Observatory WTP) | M | W: The Sugar Hollow reservoir (Observatory WTP) is 16.3 feet below overflow. Ragged Mountain reservoir is 11.5 feet below normal. Overall source water availability is at 55.5% of "full available capacity" (this includes both the South Rivanna system and the Sugar Hollow/Ragged Mountain system). Water restrictions are in excess of EO-33. |
| 6061320 | Northwestern Elementary School | Groundwater (1 well) | M | W: Significant decline in well yield. Currently hauling water to meet demand. Inspection of nearby existing well conducted last week. CFO to work rapidly with owner to connect well. |
| 2770650 | Roanoke City - Carvins Cove | Carvins Cove Reservoir/Tinker Creek/Catawba Creek | M | W: Reservoir level 34.1' below spillway - situation steadily worsening (22% of supply remaining). Approximately 200 days of storage remaining at the current rate. Mandatory restrictions imposed when reservoir level is between 26 and 30 feet below spillway (Stage 4). Suspension of all outdoor water uses with certain exceptions; cutting back on reservoir use by water purchases from Roanoke County (3-4MGD) and the City of Salem (1-2 MGD) and placing Crystal Spring (up to 2.8 MGD) into service; imposition of civil penalties and surcharge applied to base water rates. Suspension means no outside use of potable water for washing your own car, watering lawns and gardens and filling pools, etc. The 30-foot level would have triggered more drastic conservation measures (Stage 5); however, the City has maintained Stage 4 conservation measures at this time. Water restrictions are in excess of EO-33. |
| 5680200 | City of Lynchburg | Pedlar Reservoir | N | W: Pedlar Reservoir is 139" down. Drawing 3 MGD from reservoir and remainder from the James River. |
| 1195050 | Town of Appalachia | reservoir | V | W: Down 6 inches since 10/9/02; 52 MG and 91 days left, no alternate source, voluntary conservation measures. Similar conditions to '98 and '99 for this time of year. |
| 1195950 | Town of Wise | reservoir | N | W: Down 5 inches since 10/8/02; 146 MG and 225 days left; alternate creek source is still available but not in use due to turbidity in stream from runoff; no conservation measures. Worse shape than in '00 and '01 but better compared to '98 and '99 for this time of year. |
| 1195100 | Town of Big Stone Gap | Big Cherry Reservoir | V | W: Down 14 inches since 10/8/02; 115 MG or 57 days left; alternate well source is temporarily out of use after its turbidity rose drastically. Worse than normal for this time of year. Comparable to 1998 conditions for this time of year, except have alternate well source now. |
| 1720076 | City of Norton | two reservoirs in series | V | W: Down 1.5 ft 10/8/02;44.8 MG and 67 days left. Alternate source is in use, voluntary conservation measures encouraged on public access TV channel. Better than in '98, '99, and '00 for this time of year. |
| 6630050 | City of Fredericksburg | Motts Run/Rappahannock River | M | W: City of Fredericksburg (consecutive system to Spotsylvania County) has asked for mandatory conservation based on Spotsylvania County's action. |
| 3800805 | City of Suffolk | Central System | V | W: As of 10/16, reservoir system is 50.0% full in Crumps Mill. This is a 35.7% decrease from the last report. Suffolk has been pumping from Crumps Mill to Lone Star. Lone Star Lakes is at 76.5 % full a 2.5 % increase. Lone Star makes up the majority of the Northern Lakes. The Southern Lakes were at 22.5%. This is a 2.5% decrease from the last report. The city also purchases finished water from Portsmouth, which enters the central system in downtown Suffolk. As such, this system has followed the lead of the Portsmouth system and has adopted Voluntary Conservation. Suffolk will rescind Voluntary Conservation following Portsmouth's lead but not until the EDR is at full capacity. A decision concerning mandatory conservation is forthcoming. |
| 3550051 | Chesapeake - NW River system | NW River system | M | W: As of 10/16, chlorides levels in the Northwest River average 654. Monitoring well levels are at 91 % normal levels. Plant production averaged 8.35 MGD for the past week and 8.04 for the month. The ASR facility is in use to meet demand. Due to high salt and TOC levels all four surface membrane trains are in operation. 6.2 inches of rainfall this week. Because a portion of the city (a separate system from the NW River system) is served from Portsmouth, Chesapeake has decided to follow Portsmouth's lead, for ALL residents of the city. City Council voted to establish Mandatory Conservation at the meeting on 07/10/02. The restrictions took effect immediately. |
| 3830850 | Williamsburg | Waller Mill Reservoir | V | W: As of 10/16/02, Waller Mill reservoir is 29.5 inches below the spillway. Continuing to purchase 2 MGD raw water from Newport News. Supplemental well (361 gpm/0.52 MGD) has been pumping to the reservoir for about 21 months. Also getting 225,000 to 250,000 gallons per day delivered to the watershed from York County's Lightfoot water system. Voluntary conservation measures are in effect as of March 30, 2002. |
| 5117800 | Town of South Hill | Meherrin River | M | This plant has stopped operating as the new Roanoke River Service Authority waterworks began operating on 9/18/2002. |
| 6153675 | Quantico- Mainside | Lunga Reservoir/ Breckenridge reservoir | N | S: WL: Lunga 35 inches below overflow; Breckenridge full. |
| 2171250 | Stoney Creek Sanitary District |  | V | S: Well yield is off. Authority has reduced pumping capacity by 40% based on lower water table levels. Consumers have been asked to conserve water since February. Process of developing new 250 gpm well and water treatment plant. |
| 2023020 | Apple Tree | Drilled wells | M | S: Well production is lower than usual; 2 wells not in service (Steeplechase 1 & 3); water imported from and exported to AquaSource's Highland Manor system (2023415). Water restrictions are in excess of EO-33. |
| 2023480 | Rainbow Forest | Drilled wells | M | S: Well production is lower than usual, Well No.4 pump lowered and now has production; however, exporting water to AquaSource's Clearview Estates system (2023194). Water restrictions are in excess of EO-33. |
| 2161910 | Mountain View Mobile Home Park | Drilled wells | M | S: well production is lower than normal. Water levels in the wells are not routinely measured. Water restrictions are in effect per EO-33. |
| 2163550 | Maury Service Authority | Maury River | N | S: Water level approximately 6 ft above the intake |
| 3595250 | Emporia | Meherrin River | V | S: Water is still flowing over the dam. River flow and reservoir level have increased. The power plant has not been operating (voluntarily) to conserve water. |
| 3800787 | City of Suffolk | Route 17 Corridor | V | S: This system is consecutive to (purchases water from) the Portsmouth system. As such, this system has followed the lead of the Portsmouth system, and has adopted Voluntary Conservation. Since Portsmouth has gone to Mandatory Conservation, Suffolk will probably switch the supply source to their Central System (groundwater). |
| 3550050 | Chesapeake - Western Branch system | Western Branch system | M | S: This portion of the city is consecutive to (receives water from) the city of Portsmouth. Because Portsmouth decided to go on mandatory restrictions, Chesapeake has decided to follow Portsmouth's lead, for ALL residents of the city. City Council voted to establish Mandatory Conservation at the meeting on 07/10/02. The restrictions took effect immediately. Purchased water from Portsmouth at the beginning of August was averaging 3.4 MGD. After reducing the service area on 8/14/02 purchased water averaged 2.15 MGD. A decrease of 1.25 MGD. |
| 3550052 | Chesapeake - South Norfolk system | South Norfolk system | M | S: This portion of the city is consecutive to (receives water from) the city of Norfolk. Because Portsmouth decided to go on voluntary restrictions, Chesapeake has decided to follow Portsmouth's lead, for ALL residents of the city. City Council voted to establish Mandatory Conservation at the meeting on 07/10/02. The restrictions took effect immediately. Purchases from Norfolk increased from 3.8 MGD to 4.3 MGD after the service area was enlarged to lessen the burden on Portsmouth. The normal average purchased water from Norfolk was 3.6 MGD. This volume should decrease once the service area decreases. |
| 2165765 | Valley View MHP | Two drilled wells | N | S: The water system serving the park is starting to experience drought related shortages, but is not yet severe. A new waterline project that extends water service in the vicinity of this PWS has been recently completed and the water system is making the necessary arrangements with Rockingham County to connect to their new waterline. After this the MHP PWS will be inactive and will not be in a drought related problem. |
| 2015550 | Reynolds Metals Company (ALCOA) | Drilled wells | N | S: The water system has gone to a backup well due to low water production. A well site investigation was performed on 10/9/02 for a new well site; the well site approval is being forwarded on 10/16/02. |
| 2003675 | Albemarle County / Scottsville | Totier Creek Reservoirs (Scottsville WTP) | M | S: The Totier Creek Reservoir (Scottsville WTP) is full and overflowing. At this time there is adequate water to meet normal daily demands, however, the Albemarle County Service Authority has initiated mandatory water restrictions in Scottsville in addition to Crozet and the Urban area. Water restrictions are in excess of EO-33. |
| 5083550 | Town of Halifax | Banister River | V | S: the reservoir level is at full pond. Production has dropped by ~20% recently due to decreased demand. |
| 2065250 | Fluvanna Correctional Center | Mechunk Creek | M | S: The raw water impoundment is approximately 35.0% full (14 MGD available, 40 MG full capacity) and dropping. They are currently unable to pump raw water from Mechunk Creek due to low flows. The facility water demand has been reduced to approximately 95,000 due to additional use restrictions (laundry washing has been reduced from daily to 2 per week and the duration of inmate showers has been reduced). Approximately 100,000 gallons per day of water is being hauled from Lake Monticello. Water restrictions are in excess of EO-33. |
| 2065520 | Oakland School | Drilled Wells | M | S: The Oakland School waterworks provides water to approximately 150 students and staff. Four new wells have been drilled during the past two weeks. Two were dry, the third has an estimated yield of only 3 gpm, and the fourth has an estimated yield of 1 gpm. Work is underway to get these wells into operation ASAP. During this past week well production has met the daily demand and water hauling has not been necessary this past week. Water restrictions are in effect per EO-33. |
| 2125910 | NCSA - Wintergreen | Lake Monacan, Valley Ponds, Stoney Creek | M | S: The NCSA - Wintergreen waterworks source water is obtained from Lake Monacan and the Valley Ponds. Lake Monacan is 3.25 feet below normal; however, both Valley Ponds have been pumped down to minimum levels. The daily water demand is currently being met but mandatory restrictions are in effect. Water restrictions are in excess of EO-33. |
| 2125650 | Nelson County Service Authority - Schuyler | Johnson's Branch | M | S: The NCSA - Schuyler waterworks source water is obtained from Johnson's Branch. The flow is currently approximately 15 gpm (normal treatment capacity is 70 to 90 gpm). Withdrawal from Rockfish River has been continued to supplement the flow from Johnson's Branch. They are currently meeting the normal daily demand with water from the Rockfish River. Water restrictions are in excess of EO-33. |
| 2125325 | Nelson County Service Authority - Lovingston | Drilled wells | M | S: The NCSA - Lovingston waterworks source water is obtained from 11-drilled wells. During this past weeks storage tank levels have been maintained at 100% full and the daily demand is being met. Supplemental water hauling has not been necessary during the past weeks. Water restrictions are in excess of EO-33. |
| 2125202 | Johnson's Senior Center | Drilled Wells | M | S: The Johnson's Senior Center waterworks provides water to 35 nursing home residents in Nelson County. During the past weeks the well production has not met the normal daily demand. Laundry is taken off site to save water. Sufficient water is available for flushing toilets, drinking, and bathing. Water restrictions are in excess of EO-33. |
| 2065300 | Fork Union Sanitary District | Drilled Wells | M | S: The FUSD waterworks source water is obtained from 6-drilled wells. Water production is significantly below normal levels. Water restrictions have been effective, as the normally daily demand has been reduced from approximately 180,000 to 130,000 GPD. Distribution system storage was maintained at 100% during this past week and available production has been in excess of the daily demand. Mandatory water restrictions have been in effect since August 9, 2002. Water restrictions are in excess of EO-33. |
| 2015200 | Augusta County Service Authority- Deerfield | Deerfield Spring | V | S: The Deerfield Spring is drying up and reduced to a small pool in the reservoir. The new suction intake is not adequately located to maximize water collection and is being adjusted. The reservoir housing leaks and the owner (USFS) has denied requests for previous repairs that would allow for the capture and retaining of additional waters. A supplemental well has been drilled and has been connected into the treatment system on an emergency basis. Submission of plans for approval will follow. |
| 4760100 | City of Richmond | James River | M | S: The current flow in the James River is 1150 cfs whereas the normal flow for this time of year is about 1600 cfs. Richmond is having no problems with water withdrawals. The City went to mandatory water conservation on August 27, 2002. |
| 4075630 | Pagebrook (Goochland) | Groundwater | N | S: Sydnor continues to haul 2 tanker loads of water per week (5,000 gallons). |
| 6137500 | Wilderness WTP | Rapidan River | M | S: Stream flow is very low. Temporary pumps are available to get water to intake structure. |
| 6113200 | Town of Madison | White Oak Run | M | S: Stream flow is very low, but no adverse impact on water treatment plant to this point. |
| 6137500 | Town of Orange | Rapidan River | M | S: Stream flow is very low, and temporary raw water pumps are available for use when flow recedes away from intake structure. Dam repair is continuing and completion date is approximately 7-10 days. Estimated that 400,000 GPD is lost through existing dam. Emergency raw water sources near Culpeper and Gordonsville have been sampled with no adverse contamination revealed thus far. Corps of Engineers met with town, county, and state officials several weeks ago to discuss various emergency water supply alternatives. COE can design, build, and pay for transporting raw or finished water. Town's options include hauling finished water from Culpeper and hauling or piping raw water from Culpeper or Gordonsville. Town and county officials met with USDA technical and financial staff last week to discuss money available to pay for temporary and long-term solutions. |
| 2171750 | Strasburg | North Fork Shenandoah River | V | S: Stream flow has increased due to recent rains - at 258 cfs (166.5 MGD) on 10/16; intake water level still above 1999 drought levels; considering measures to raise intake water levels; maintaining normal pumping rates. |
| 2187522 | High Knob Subdivision | Springs and wells | N | S: Spring yields have dropped significantly and wells are being increasingly relied upon to meet water demand. |
| 2043250 | Boyce-Millwood | Prospect Hill Spring | V | S: Spring yield is down from normal historical levels. Voluntary measures instituted to reduce water demand. Grouting of the outside area around the spring enclosure has stopped some of the water loss. Development of additional water sources is being investigated |
| 1071525 | Marville Subdivision | spring | N | S: spring is low to dry; Giles County is hauling water to residents. |
| 6177280, 6177300 | Spotsylvania County | Ni River Reservoir and Motts Run/Rappahannock River | M | S: Spotsylvania County declared a water emergency in mid November and instituted mandatory conservation. Ni River Reservoir is 47% full (64 inches below normal). Motts Run Reservoir is 69% full (6.9 feet below normal). Flow in Rappahannock River is at 1-3% mean annual flow. Estimated approximately 365-supply remaining. |
| 5019400 | High Point Subdivision | Smith Mountain Lake | N | S: Smith Mountain Lake is 3.5' below full pond |
| 6179100, 6179775 | Stafford County | Smith Lake and Abel Lake | M | S: Smith Lake is 101 inches below normal and Abel Lake is 101 inches below normal. Estimated 254-day supply remaining. |
| 2165300 | Food Processors | North Fork Shen | N | S: Several feet above the intake, water is approximately at the level of the dam with very little flowing over the spillway. |
| 5031175 | Town of Brookneal | Phelps Creek Reservoir | N | S: Reservoir overflow at 100,000 GPD. Estimated reserve below spillway 287 days. |
| 2161700 | Roanoke County WTF | Spring Hollow Reservoir and 8 wells | M | S: Reservoir level 33.6 feet below normal; 196.4 feet of water remaining in the reservoir or approximately 180 days of storage left at the current usage rate and without pumping from the Roanoke River (average flow rate 40.65 cfs). Water restrictions general follow EO-33; except the county's rules are stricter on car washing but allow watering of golf courses and athletic fields. Water is exported to the City of Roanoke system (2770650). |
| 5019250 | Eagle Eyrie | Unnamed Reservoir | N | S: Reservoir is down 9.5'. Engineer estimates 50 days of storage. Looking into existing wells to supplement supply. Identified and repaired leak on the waterline from intake to plant. Long term plan is to connect to BCPSA. |
| 5515050 | City of Bedford | Stoney Creek Reservoir | M | S: Reservoir is 39 inches down. City is drawing about 0.50 MGD from four wells and river to supplement reservoir. City went to mandatory conservation. |
| 6059500 | FCWA-Lorton/Occoquan WTPs | Occoquan Reservoir | N | S: Reservoir 71% full, 5.69 billion gallons usable storage. All of FCWA service area is on "watch" status. |
| 2023415 | Highland Manor | Drilled wells | M | S: only two wells producing water (Rosemae and Carolyn); water exported to and imported from AquaSource's Apple Tree system (2023020). Water restrictions are in excess of EO-33. |
| 5135110 | Town of Burkeville | 7 wells | M | S: one well has lost production others showed signs of stress. Water conservation in place for ~10 weeks. At reduced output wells seem to be working satisfactorily |
| 3095490 | James City Service Authority Central System | Approximately 30 wells | V | S: No significant impact on water levels in wells. Conservation due to high demands in distribution system. |
| 2163250 | Town of Goshen | Goshen Spring | M | S: No reported drop in spring yield, but a news article came out in the local weekly paper. Essentially mandating water conservation and setting an ordinance that residential customers may not allow water to be taken by or given to non-town residents. The Town Council is attempting to decide how to proceed with funding for several much-needed infrastructure improvements that will reduce leakage and unaccounted for water. |
| 3183550 | Jarratt | Nottoway River | N | S: No quality or quantity problems noted. The river level and rate of flow have decreased. |
| 3670800 | Virginia-American, Hopewell | Appomattox River/James River | M | S: No problems with water quantity. Flow has increased this week in both the James River and Appomattox River. Dissolved minerals have decreased slightly, with some effect on industrial consumers and disinfection byproducts. Water quality is still fluctuating with changes in the tide. City of Hopewell enacted water conservation ordinance to mirror EO33 on September 10 |
| 6047500 | Town of Culpeper | Lake Pelham | N | S: No problems at this time. Reservoir is near normal level for this time of year. |
| 6061600 | Town of Warrenton | Warrenton Reservoir | N | S: No problems at this time. Main reservoir is near normal level for this time of year. |
| 2163075 | Brownsburg Water Company | Drilled wells | V | S: No defined problems have occurred and they have requested voluntary restrictions as a precaution. |
| 2165060 | Broadway, Town Of | North Fork Of Shenandoah, Linville Creek | N | S: N. Fork and Linville approximately 1 foot above the intakes. Are using Linville creek only at this time. |
| 2790600 | Staunton | North River Dam, Middle River | N | S: Middle River is not in use, flow reduced last week from North River from 1.8 MGD to 1.0 MGD. No problems noted at Gardner Springs. Water level is approximately 3.9 feet lower than normal at the dam, but can drop to 17 feet below normal without much impact. |
| 2165045 | Bridgewater, Town Of | North River | N | S: lowest observed in 25 years, several feet above the intake, approximately 11MGD at the intake |
| 5690400 | City of Martinsville | Beaver Creek Reservoir | M | S: Last reservoir check at 9.1' below spillway--in order to help reduce loss in reservoir, the City continues to use Leatherwood source along with reservoir and pumping at ~2 MGD from this source--has been holding up since recent rainfall; Note City implemented voluntary conservation measures on 8/27/02 |
| 6033425 | Lake Caroline | Lake Caroline | M | S: Lake Caroline is 23 inches below normal level. Estimated 280-day supply remaining. |
| 6059501 | FCWA-Corbalis WTP | Potomac River | N | S: Jennings Randolph and Little Seneca reservoirs in the Potomac River watershed are at 64% full and 80% full, respectively, on 9/17/02. Flow In Potomac River at Little Falls (downstream of the Wash. Met.intakes) on 10/16/02 was 2500 MGD. Releases from upstream Jennings Randolph Reservoir were halted on September 23 due to increased river flow caused by rains in the upper watershed. Releases from Little Seneca were stopped on Sept 14. All of FCWA service area is on "watch' status. Voluntary conservation will be instituted when the upstream reservoirs drop below 60% full. No releases were made from the reservoirs in 2000 or 2001. Reservoir storage is adequate to meet the water supply needs in the event the 1930-31 drought of record were to re-occur. |
| 2187406 | Front Royal | South Fork, Shenandoah River | M | S: Implemented mandatory restrictions per Governor's policy. Running 14-day average is well below 30% mean stream flow [17.51% with mean stream flow at 316 cfs (203.9 MGD) on 10/16]. VWPP requires conservation controls be implemented at 30% (voluntary), 17% (mandatory), 15% (emergency), and 13% (rationing) of mean stream flow based on 14-day running average. |
| 4999999 | Henrico County | Purchased from the City of Richmond | M | S: Henrico County has an emergency ordinance in place, which allows them to enact mandatory water restrictions. Henrico County's decision to go to mandatory restrictions is driven by demand (tank levels) or a decision by the City of Richmond to go to mandatory restrictions. Following the City's lead, the County went to mandatory water conservation on August 27, 2002, conservation measures are being enforced. |
| 6033100 | Caroline | Campbell's Creek (groundwater) | M | S: Hauling water (approx 10,000 GPD) from county system. Recently drilled well has yield of approx. 30 gpm and samples will be collected this week for complete chemical analysis. Waterline extension from county being considered. |
| 4085398 | Hanover County | North Anna River, wells, and purchased water from the City of Richmond | M | S: Hanover County has an ordinance in place with triggers for mandatory water restrictions. Mandatory water conservation is triggered if (1) either the City of Richmond or Henrico County goes to mandatory restrictions or (2) low flow in the North Anna River as determined by DEQ. Following the City's lead, the County went to mandatory water conservation on August 27, 2002. M - the County is enforcing the conservation measures in their main service area only. |
| 6600100 | City of Fairfax | Goose Creek/Beaver Dam | N | S: Goose Creek Reservoir is 1 inch over top of dam, and Beaver Dam Reservoir is 8.95 feet below full. |
| 6107600 | Purcellville | Hirst Reservoirs | V | S: Front reservoir 3.4 feet below full; back lake is 4.0 feet below full. Drought "watch" status still in effect. Mandatory restrictions go into effect when front lake reaches 5 feet below normal. |
| 2065480 | Lake Monticello Service Company Aqua Source | Rivanna River | M | S: Flows in the Rivanna River at the Lake Monticello Water Treatment Plant are extremely low, however there is currently a sufficient quantity of raw water to meet daily demands. Mandatory water restrictions are in effect. Water restrictions are in excess of EO-33. |
| 2079625 | Rapidan Service Authority | Rapidan River | M | S: Flows in the Rapidan River at the Greene Water Treatment Plant are extremely low, however there is currently a sufficient quantity of raw water to meet daily demands. Mandatory restrictions were initiated on August 23, 2002. Water restrictions are in excess of EO-33. |
| 5089376 | Fieldcrest Cannon WTP | Smith River | M | S: flow subject to release from Philpott Dam |
| 5089852 | Upper Smith River WTP | Smith River | M | S: flow subject to release from Philpott Dam |
| 5007030 | Amelia Academy | Well No.1 (bored) | M | S: Existing well is very low. We are awaiting plans for a new well, but will allow it's emergency connection if necessary. |
| 2023194 | Clearview estates | Drilled wells | M | S: currently no production from the two Clearview Estates wells - importing water from AquaSource's Rainbow Forest system (2023480). Water restrictions are in excess of EO-33. |
| 6685100 | City of Manassas | Lake Manassas (Broad Run) | N | S: Current WL 284.02 feet; Max is 290 feet. Mean elevation for September is 286.68 feet. Stage 1 conservation (voluntary) will start at reservoir elevation 279.72 feet. |
| 6107300 | Leesburg | Potomac River | V | S: Current river level at 188.2 feet. Normal level is 187.50 feet. Leesburg intake is located upstream of the FCWA and Wash. Met. Intakes. Signs requesting voluntary conservation have been placed around town and on town website. |
| 2015575 | South River S.D. (ACSA) | Coles Run | N | S: Coles Run reservoir level is reported to be almost full. No impact on system due to multiple sources. |
| 2003250 | Albemarle County / Crozet | Beaver Creek Reservoir | M | S: Beaver Creek Reservoir is currently down 5.3 feet from normal full. The RWSA currently able to meet normal demands. Water restrictions are in excess of EO-33. |
| 5031200 | Dan River, Inc. - Brookneal Plant | Falling River | N | S: Approx. 1 inch of water over spillway, though intakes still adequately covered. Going to connect to Town water system for drinking water. |
| 5031150 | CCUSA | Otter River | N | S: 19" above intake screen. Terminal Reservoir is full. Recent rain on watershed greatly improved reservoir levels. |
| 5009050 | Town of Amherst | Buffalo River | M | B: Water is being released from a County-owned upstream Mill Creek Reservoir into the Buffalo River to provide water for the Town. Mill Creek is down about 9". Recent rain has allowed Town to throttle reservoir valve. This should increase reservoir storage. Town is planning to drill well to supplement supply. |
| 5111800 | Town of Victoria | Nottoway Falls & Lunenburg Lake | M | B: Water is 4 inches over dam. They are trying to follow the Governors recommendations. Production has dropped by 20% after fixing leaks. |
| 1071455 | Giles County PSA membrane WTP | well | V | B: Two well standby sources still in use. New River well recharge is improving; water level at 80 ft above well pump at 2 MGD pumping rate. |
| 5143210 | Town of Gretna | Georges Creek Reservoir | M | B: Town reservoir full; No longer pumping from temporary impoundment of tributary to Whitethorn Creek or from Elba spring into the reservoir; Town initiated mandatory conservation measures beginning 8/7/02. |
| 4041035 | Appomattox River Water Authority | Lake Chesdin | M | B: The water level is 62 inches below the top of the dam. A week ago the level was 69 inches below the top of the dam. Wholesale water provided - but following the Governor's EO for mandatory conservation |
| 5147450 | Town of Farmville | Appomattox River | M | B: The river depth increased 3 inches to ~ 38 inches. They are operating normally but still retain their water conservation measures as before. Their average reduction in usage is still ranging between 50,000 and 100,000 GPD less than normal. They still aren't using the Holiday Lake siphon. The 2 emergency wells are still awaiting the completion of analyses. |
| 5111450 | Town of Kenbridge | Flat Rock Creek & reservoir | M | B: The reservoir level is at 4 feet and increasing. They're pumping 1.5 MGD into the reservoir from Flat Rock Cr., which is at 7 inches above full pond. |
| 4041845 | Swift Creek WTP (Chesterfield County) | Swift Creek Reservoir | M | B: The reservoir level is 173.8 feet. The level is 0.1 feet higher than it was a week ago and 3.2 feet below the top of the dam. Mandatory water conservation has been in effect since August 16, 2002. |
| 4075735 | James River Correctional Center | Beaverdam Creek and the James River | M | B: The flow in the primary source of water (Beaverdam Creek) is now sufficient to meet the needs of the water treatment plant without being supplemented by water pumped from the James River. Besides supplying water to its normal customers, this WTP is now supplementing the water supply at Nottoway Correctional Center in Nottoway County. Trucks hauled 200,000 gallons from James River Correctional Center to the Nottoway Correctional Center last week. Mandatory water conservation is in effect for the correctional units. They are on "code yellow". |
| 5780600 | Town of South Boston | Dan River | V | B: The Dan River is a little higher, 3 feet deep at the intake screen. This is not restricting plant operation. They indicate they are utilizing the Governor's conservation guidelines but noted that little reduction in demand has been observed. They are discussing ways to improve enforcement. |
| 4073311 | Gloucester | Beaverdam Reservoir | V | B: The Beaverdam Reservoir water overflow elevation is 40.5. The water level was 39.13 on October 15, 2002. The reservoir level has risen since the last report. Note that about a million gallons of water is allowed to flow through the reservoir every day. V - but following the Governor's EO for mandatory conservation. |
| 6107200 | Town of Hillsboro | GWUDISW (Spring) and newly drilled well | V | B: Spring flow declined to approx. 3.25 gpm several weeks ago is now holding steady. New well drilled July 6-8, 2002, using DWSRF planning grant money; yield approx 8 gpm. Well temporarily connected to system. CFO continues to work with town to get well permanently connected ASAP. |
| 3650150 | Ft. Monroe | Big Bethel Reservoir System | V | B: Reservoirs are full! Last report- the lower reservoir was 15.25 inches below the spillway; the upper reservoir was 20 inches below the spillway. Readings from 10/16/02. |
| 5029085 | Buckingham County Waterworks | Troublesome Creek Reservoir | V | B: Reservoir rose to ~29-inches below spillway. They are still using a portable pump to transfer water into the raw water pump station from the reservoir. They have passed an emergency ordinance as planned and will have a public hearing in November. |
| 5037300 | Town of Keysville | Spring Creek Impoundment | M | B: Reservoir is at full pond. They are following the Governors guidance criteria and passed an emergency ordinance this week to restrict water usage. A recently constructed farm pond may have cut off a spring that recharges this 42-acre reservoir. |
| 5135160 | Town of Crewe | Lazerretto Creek/Crystal Lake | M | B: Reservoir is 3 inches above the overflow. They had 1.4 inches of rain last night. Restrictions on water use still utilize the Governor's guidance criteria. They will return to more restrictive conservation measures if the reservoir falls more than 6 inches below the overflow. Piedmont Hospital has shut down their well system (not due to drought but because of long term contamination problems) and is supplied completely by the Town. Nottoway Correctional Center is fully on the Town's system now. The operator noted some sporadic increases from one or more of these State owned facilities. |
| 5135100 | Town of Blackstone | Nottoway River Reservoir | M | B: Nottoway Reservoir is full with minimal overflow. |
| 5117310 | Town of Clarksville | Kerr Lake | N | B: Kerr Lake is approximately 5 feet below normal pool. |
| 5067840 | Town of Rocky Mount | Blackwater Creek | M | B: Have 2.5 inches overflow at the check dam; The Town is not under any sort of conservation. If necessary the plant could cut back pumping rate and extend operating hours to maintain flow. |
| 5025450 | Town of Lawrenceville | Great Creek | N | B: Great Creek Reservoir is approximately 22" below maximum pool but this is not causing problems according to their operator. |
| 5009250 | Amherst County Service Authority | Graham Creek Res., Harris Creek | M | B: Drawing from creek as much as possible (a few hours a day), but almost entirely from reservoir, which is 55.5" down. Emergency line from the James River was completed on 9/16. Started mandatory water restrictions July 24, 2002. Pumping water from James River to reservoir. |
| 5089487 | Marrowbone Cr. WTP | Marrowbone Creek | M | B: Creek is still flowing over check dam and plant operating at design capacity of 1 MGD. Not pumping from upstream reservoir; Local mandatory conservation measures in place since 7/16/02 have been lifted (still complying with statewide mandatory conservation measures) & now using single interconnection with City of Martinsville to supplement system. |
| 5031050 | Town of Altavista | Staunton River, Reed Creek | V | B: Creek intake not in use because water level is too low; The two springs have lost capacity. Using Staunton River as primary source. Approximately 2.1 inches of rain over the weekend has improved flows. |
| 1077240 | Town of Fries | Eagle Bottom Creek & New River | N | B: Creek has recovered sufficiently so that pumping from New River is no longer necessary. |
| 5143114 | Town of Chatham | Cherrystone Creek | M | B: Creek flow improved some with recent rain- operating at full capacity at this time |
| 5590100 | City of Danville | Dan River, Schofield Dam | N | B: City is having no problems meeting their average demand of 7.0 MGD. |
| 3700500 | Newport News | Chickahominy, Little Creek, Diascund, Skiffes Creek, Harwoods Mill and Lee Hall Reservoirs | V | B: As of 10/15/02, the reservoirs were 59% full (in the previous report the reservoirs were 58% full). One pump on at the Chickahominy pump station. Blending river water with Little Creek Reservoir for chloride moderation. Upstream of the dam (intake), chlorides are about 840 PPM. Went to Voluntary Conservation effective 07/25/02. Mandatory Conservation starts 10/18. RO plant producing of about 3.65 MGD. |
| 3740600 | Portsmouth | Lakes Cohoon, Meade, Kilby, and Speights Run | M | B: As of 10/15, reservoirs are at 59% of useful capacity. This is a 4 % increase since 10/07. Historic avg. capacity for this time of year is 88% and the monthly median is 94%. Both emergency wells are ON, pumping an average of 4.5 MGD. Est. days of reservoir storage remaining at current raw water pumpage of 15.1 MGD is about 151 days. City Council voted to establish Mandatory Conservation (Condition II) at meeting of 07/09/02. An interim conservation step, before going to Condition III, will be brought before City Council should the reservoir capacity drop to 50%. Interim conservation step imposes a 25% surcharge on all customers who exceed 600 cu. ft. (avg. 74 GPD) per bimonthly billing cycle. Condition III trigger occurs when reservoir capacity reaches 40%. Condition III imposes a more severe rate penalty. Both the interim step and Condition III must be passed by City Council prior to implementation. City is beginning negotiations, and preliminary design of a raw water line, to provide Lake Gaston water to the treatment plant. |
| 3710100 | Norfolk | Lake Prince, Lake Burnt Mills, Western Branch reservoir, Nottoway River, Blackwater River, 4 western wells; Little Creek reservoir, Lakes Smith, Lawson, Whitehurst, and Wright. Lake Gaston. | N | B: As of 10/14, reservoirs are at 82.7% of total capacity. This is a 2.7% increase since 10/07. Historic reservoir capacity at this time of year is 80.5%. Reservoirs are the Western Branch Reservoir, Lake Prince, Burnt Mills Reservoir, and the in-town lakes. Surface water sources pumped into the reservoirs are Lake Gaston, Nottoway River and Blackwater River. There are also four groundwater wells which discharge to the reservoirs. Avg. pumping into the reservoirs from Lake Gaston = 31.6 MGD; Blackwater River = 0 MGD (pump off 08/02); Nottoway River = 21.7 MGD. Deep wells = 0 MGD (pumps off 09/24). Estimated 176 days of storage on reservoirs alone with no pumpage from the surface water sources or wells into the reservoirs, based on current pumpage to the treatment plants. Currently not under locally imposed conservation measures but honoring Governor's Order. |
| 5141640 | Town of Stuart | South Mayo River | N | B: About 1.8 inches overflowing spillway. Started pump test and sampling of two inactive wells. |

##### APPENDIX I

Virginia Department of Health Drought Watch Public Water Systems (October 18, 2002)

| PWSID 1-Abingdon 2-Lexington 3-Southeast VA 4-East Central 5-Danville 6-Culpeper | Waterworks | Source Name | Restrictions N: No M: Mandatory V: Voluntary | Situation B: Better, S: Same/Stable, W: Worse |
| --- | --- | --- | --- | --- |
| 1071525 | Marleville Subdivision | spring | N | S: spring is low to dry; Giles County is hauling water to residents.Soon to connect to PSA. |
| 1195050 | Town of Appalachia | reservoir | V | W: Down 6 inches since 10/9/02; 52 MG and 91 days left, no alternate source, voluntary conservation measures. Similar conditions to '98 and '99 for this time of year. |
| 1195100 | Town of Big Stone Gap | Big Cherry Reservoir | V | W: Down 14 inches since 10/8/02; 115 MG or 57 days left; alternate well source is temporarily out of use after its turbidity rose drastically. Worse than normal for this time of year. Comparable to 1998 conditions for this time of year, except have alternate well source now. |
| 3700500 | Newport News | Chickahominy, Little Creek, Diascund, Skiffes Creek, Harwoods Mill and Lee Hall Reservoirs | V | B: As of 10/15/02, the reservoirs were 59% full (in the previous report the reservoirs were 58% full). One pump on at the Chickahominy pump station. Blending river water with Little Creek Reservoir for chloride moderation. Upstream of the dam (intake), chlorides are about 840 PPM. Went to Voluntary Conservation effective 07/25/02. Mandatory Conservation starts 10/18. RO plant producing of about 3.65 MGD. |
| 3830850 | Williamsburg | Waller Mill Reservoir | V | W: As of 10/16/02, Waller Mill reservoir is 29.5 inches below the spillway. Continuing to purchase 2 MGD raw water from Newport News. Supplemental well (361 gpm/0.52 MGD) has been pumping to the reservoir for about 21 months. Also getting 225,000 to 250,000 gallons per day delivered to the watershed from York County's Lightfoot water system. Voluntary conservation measures are in effect as of March 30, 2002. |
| 4075630 | Pagebrook (Goochland) | Groundwater | N | S: Sydnor continues to haul 2 tanker loads of water per week (5,000 gallons). |
| 4087860 | Tuckaway West Child Care Ctr. | well | M | S: Water system cannot handle high demand. Mandatory program implented for school. Also, voluntary conservation requested by all localities in greater Richmond area. |
| 5007135 | Amelia Courthouse | well | M | W: 1 well lost capacity- another larger well being developed- geologist recommended well be monitored closely-well levels have not been monitored, but will be. |
| 5011050 | Appomattox, Town Of | well | M | W: 4 of 7 wells are low 5-9 ft (one is 5' and three are 9') other 3 wells 1-3 ft |
| 5019425 | Hillcrest Subdivision | well | M | W: near critical - periodic well failure under high demand |
| 5029085 | Buckingham County Waterworks | Troublesome Creek Reservoir | V | B: Reservoir rose to ~29-inches below spillway. They are still using a portable pump to transfer water into the raw water pump station from the reservoir. They have passed an emergency ordinance as planned and will have a public hearing in November. |
| 5031825 | Suburban Trailer Town, Inc. | well | M | W: Well 5 essentially non-producing; Well 4 lost ~80% of capacity; Well 3 lost !75% of capacity; contribution from Well 2 is negligible; has purchased some water |
| 6033050 | Campbell Creek Subdivision |  | M | W: |
| 6061320 | Northwestern Elem School |  | M | W: Believe that well has dried up. |
| 6107033 | Banneker Elementary School |  | M | W: water table down |
| 6137500 | Town of Orange | Rapidan River | M | S: Stream flow is very low, and temporary raw water pumps are available for use when flow recedes away from intake structure. Dam repair is continuing and completion date is approximately 7-10 days. Estimated that 400,000 GPD is lost through existing dam. Emergency raw water sources near Culpeper and Gordonsville have been sampled with no adverse contamination revealed thus far. Corps of Engineers met with town, county, and state officials several weeks ago to discuss various emergency water supply alternatives. COE can design, build, and pay for transporting raw or finished water. Town's options include hauling finished water from Culpeper and hauling or piping raw water from Culpeper or Gordonsville. Town and county officials met with USDA technical and financial staff last week to discuss money available to pay for temporary and long-term solutions. |