MEMORANDUM

August 13, 2008

To:		Elaine Manning, EPA/OAQPS

From:		Chris Holder and Dave Burch, ICF International

Subject:	Summary of Estimated Cancer Risks for the Halogenated Solvent Cleaning Source Category using the 1999 and 2002 National Emissions Inventory, Including Risks Specific to Individual Facility Sectors

1.	Introduction

On May 3, 2007, EPA published a rule under its Residual Risk Program which regulates the emissions of hazardous air pollutants from halogenated solvent cleaning machines.  Risk assessments done in support of this rule can be found in the rule docket.  Recently, ICF conducted an additional risk assessment for EPA using a set of facility emissions data from the 1999 and 2002 National Emissions Inventory (NEI).  These new assessments differ from the previous assessment primarily in that individual industry sectors within this category were modeled separately.  These facility sectors are identified as narrow tube, continuous web cleaning, military depot, aerospace, and all remaining facilities in the category not identified as being part of these four sectors.  This sector-based analysis expands upon the results of the previous non-sector-based assessment by again evaluating the risks under an emissions control level of 40,000 kg/yr methylene-chloride (MC)-equivalent emissions and comparing them to risks at baseline (uncontrolled) emissions for all the sectors.  Additionally, the emission control levels of 60,000 (which was the limit included in the residual risk rule for certain sectors of this source category) and 100,000 kg/yr MC-equivalent emissions are evaluated.  These new results are not meant to replace the previous risk assessments but are meant to complement them.  As was done previously, cancer risks for the baseline and 60,000 kg/yr control level were estimated using two available cancer unit risk estimates (UREs) for the carcinogen perchloroethylene (PCE): a value developed by the California EPA (CalEPA) and a value developed by the EPA’s Office of Prevention, Pesticides and Toxic Substances (OPPTS).

The datasets and methodology used in this study are described in Section 2.  The risk results of this study, and comparisons to previous risk assessments, are provided in Section 3.  The discussion in Section 4 summarizes this assessment.  Appendix A describes the probabilistic analysis employed.  Appendix B provides selected NEI data fields for this source category, including latitude/longitude and chemical-specific emission rates.  Appendix C contains the stack parameters as defined for this analysis.  Appendix D contains the facility IDs and names for each of the four halogenated solvent cleaning facility sectors, including those not emitting known carcinogens.  Appendix E contains selected fields, such as facility-total emissions using the CalEPA and OPPTS UREs, from the modeling input files for this source category.

2.	Methodology and Data

The modeling and risk characterization methods used in these risk assessments were identical to those employed originally.1 The analyses described in this memorandum were performed to evaluate the specific impacts of methylene-chloride (MC)-equivalent emission limits of 40,000, 60,000, and 100,000 kg/yr for each facility in the entire source category and for each facility identified in the four industry sectors.   In addition, the results for annual cancer incidences and for the number of facilities at each risk level were scaled up to reflect the national-scale impacts (EPA has estimated that there are approximately 1,900 halogenated solvent cleaning facilities in the country).

Risks were also adjusted to reflect population mobility and residence time (see Appendix A).  The current assessment used an updated version of the Johnson and Capel (1992) population mobility model, where estimations of residence time for long-term residence have been improved.  In order to see the effects of these newer data on this risk assessment, we redid our baseline risk assessment using the 1999 NEI halogenated solvent cleaning inventory.  These emissions were the data used in EPA’s August 17, 2006, risk assessment to support the rule proposal.  The newer residence time distribution used in the current assessment was shifted such that individuals spend more time in each residence location than was predicted using the older distribution.  The expected result of that shift is that an individual who is in a higher risk category stays there longer and, therefore, has a higher lifetime risk.  It should be noted that neither the maximum individual risk (MIR) nor the population-level annual cancer incidence estimates are affected by this shift in the residence time distribution.

2.1.	Emissions and facility data

The 1999 National Emissions Inventory (NEI) database for the halogenated solvent cleaning source category identified 1,167 halogenated solvent cleaning facilities in all, with only 743 emitting hazardous air pollutants (HAPs) that are known carcinogens (i.e., HAPs for which cancer unit risk estimates (UREs) have been assigned by EPA).  When scaled up to reflect the national scope of the rule (i.e., using the scaling factor of 1,900/1,167), we estimate 1,900 facilities with 1,210 facilities emitting one or more known carcinogens.

The 2002 NEI database identified 1,080 halogenated solvent cleaning facilities in all, but only 734 of these facilities reported emissions of HAPs that are known carcinogens.  Scaling-up these numbers by a factor of 1,900/1,080 yields 1,900 facilities with 1,291 facilities emitting one or more known carcinogens.

The remaining facilities only emit non-carcinogen solvents (e.g., 1,1,1-trichloroethane (TCA)). Therefore, the risk results presented here include risk estimates only from the 1,210 and 1,291 “carcinogen-emitting” facilities estimated based on those identified in the 1999 and 2002 databases, respectively (see the 1999 and 2002 halogenated solvent cleaning NEI data in Appendix B).  Chemical-specific emission rates and facility locations for modeled facilities were defined according to the latitude and longitude locations reported in the 1999 and 2002 NEI.  One facility location was corrected in the 2002 NEI input compared to the model runs performed previously: facility NEI-7347, noted previously as being at 40.23332 °N -75.5528 °W, was corrected to 40.19417 °N -75.4847 °W.  Chemical-specific emission rates and latitude-longitude locations of facilities in the halogenated solvent cleaning source category in the 1999 and 2002 NEI are presented in Appendix B.

Stack parameters used to model all facilities were identical to those used in the residual risk assessment for the final rule; values were based on facility data from the 1999 NEI as described in the 2006 Risk Assessment Report.  These stack parameters are presented in Appendix C.

2.2.	Sector Subsets

Industry sectors were identified based on either the uniqueness of their cleaning machines (i.e., their size), their cleaning process, or their products (e.g., very narrow tubes used in the biomedical industry).  Each of these sectors is described below.  For the aerospace and ‘other’ sectors, differences between the numbers of facilities shown in the following section and the numbers of facilities presented in each exhibit are due to the use of the scaling factors for these sectors (see previous subsection).

2.2a.	Aerospace

In all, 114 (66 carcinogen-emitting) aerospace facilities were identified from the 1999 NEI and 97 (67 carcinogen-emitting) from the 2002 NEI. These facilities are listed in Exhibit D-1. To identify aerospace facilities from among all halogenated solvent cleaning facilities, the following criteria were used to search the 1999 and 2002 NEI databases:

- Standard Industrial Classification (SIC) corresponding to: 3720, 3724, 3728, 3760, 3761, 3764, 3769, 4512, and 4581.

- North American Industrial Classification System (NAICS) codes corresponding to: 3336411, 336412, 336413, 336414, 336419, 381111, 481112.

- Keywords in facility name corresponding to “*air*” and “*aero*”.

2.2b.	Military Depot

In all, 2 (all carcinogen-emitting) military depot facilities were identified from the 1999 NEI and 3 (2 carcinogen-emitting) from the 2002 NEI.  These facilities are listed in Exhibit D-2. To identify military depot facilities from among all halogenated solvent cleaning facilities, the following criteria were used to search the 1999 and 2002 NEI databases:

- SIC corresponding to: 9711.

- Subjective check where each military depot facility’s description (from their respective websites) was compared to the Military Depot Maintenance Facility description from the preamble to the final rule (p. 25143), specifically:

“…solely for the purpose of repairing, modifying, converting, and refitting worn and/or damaged military assets for redistribution to military units and subject to the 1994 [National Emissions Standards for Hazardous Air Pollutants].”

2.2c.	Narrow Tube

In all, 10 (all carcinogen-emitting) narrow tube facilities were identified from the 1999 NEI and 14 (all carcinogen-emitting) from the 2002 NEI.  These facilities are listed in Exhibit D-3. To identify narrow-tube-producing facilities from among all halogenated solvent cleaning facilities, the following criteria were used to search the 1999 and 2002 NEI databases:

- Keywords corresponding to “*tube*”.

- Those tube facilities only producing tubes with outside diameters of 0.25 inches or smaller (tube size information obtained from facility web pages and comment letters which may be found in the rule docket).

2.2d.	Continuous Web Cleaning

In all, 10 (9 carcinogen-emitting) continuous web cleaning (CWC) facilities were identified from the 1999 NEI and 8 (7 carcinogen-emitting) from the 2002 NEI.  These facilities are listed in Exhibit D-4. To identify CWC facilities from among all halogenated solvent cleaning facilities, the following criteria were used to search the 1999 and 2002 NEI databases:

- Analyzing facility comment letters to identify facility operations.

2.2e.	Other

In all, 1,031 (656 carcinogen-emitting) halogenated solvent cleaning facilities not corresponding to the above four sectors were identified from the 1999 NEI and 958 (644 carcinogen-emitting) from the 2002 NEI.

2.3.	Control Options

In addition to calculating cancer risk for a baseline scenario, we evaluated the emission control level of 60,000 kg/yr, expressed as MC equivalents.  This control level was selected as the emission limit included in the final residual risk rule for certain sectors of the halogenated solvent cleaning source category. As with the previous assessment, the more conservative emission control level of 40,000 kg/yr was also evaluated, as was the less conservative control level of 100,000 kg/yr.  The calculation of the MC-equivalent emissions is described in the August 4, 2006, risk report cited above.

As was done for the residual risk assessment, we evaluated risks separately using the California EPA (CalEPA) URE for perchloroethylene (PCE) of 5.9 × 10-6 (μg/m3)-1 and a URE for PCE developed by EPA’s Office of Prevention, Pesticides and Toxic Substance (OPPTS) of 7.1 × 10-7 (μg/m3)-1.  The 1999 and 2002 NEI halogenated solvent cleaning modeling files are provided in Appendix E.  Both UREs were evaluated for the baseline and 60,000 kg/yr emissions control levels, while the 40,000 and 100,000 kg/yr analyses were limited to the CalEPA URE for a simplified comparison to the baseline emissions and the 60,000 kg/yr control.

3.	Results

The results of this risk assessment are presented in Exhibits 1a and 1b through 6a and 6b.   The risk metrics estimated include maximum individual risk (MIR), the annual lifetime cancer incidence (hereafter “incidence”) from the modeled population, and the distribution of individual lifetime cancer risk in the modeled population after residence time modifications (hereafter “risk”).  As in the previous risk results for this source category, individual cancer risk was estimated based on the assumption of continuous lifetime (i.e., 70-year) exposure at the assumed receptor locations (i.e., census block centroids).  Population risk estimates have been adjusted to reflect variations in individual residence times (i.e., exposure) as discussed briefly in Appendix A and in more detail in the 2006 Risk Report.1

3.1.	Comparison with Halogenated Solvent Cleaning Category Risk Assessments Done Previously

Exhibits 1a and 1b present the risk results for the entire inventory of halogenated solvent cleaning facilities identified in the 1999 and 2002 National Emissions Inventory (NEI) databases.  For 1999, the baseline risk assessment (based on the California EPA (CalEPA) unit risk estimate (URE) for perchloroethylene (PCE)) was associated with an MIR of 200 in a million with an incidence of 0.66 cases/yr (Exhibit 1a).  These results are comparable to those presented in the risk assessment report done in support of the proposed rule.  The difference seen in the incidence numbers between these two sets of results (0.41 cases/yr at proposal versus 0.66 case/yr now) is due to the fact that the incidence numbers at the time of the proposed rule were not scaled up to account for the fact that only about two-thirds of the total estimated number of sources in the category were included in the assessment.  When the appropriate scale-up factor of 1.6 is applied to the incidence of 0.41 cases/yr, the result was 0.66 cases/yr.

When the 60,000 kg/yr control level was applied to all facilities using the CalEPA URE for PCE, the MIR was reduced to 30 in a million with an incidence of 0.35 cases/yr (Exhibit 1a).  These 60,000 kg/yr results agree with the MIR of 30 in a million and incidence of 0.34 cases/yr (0.21 x 1,900/1,167) presented for this control level in the risk assessment supporting the proposal.

Using the 2002 NEI inventory and the CalEPA URE for PCE, we estimated the baseline MIR to be 100 in a million with an incidence of 0.55 cases/yr (Exhibit 1a).  These results agree with those reported in the risk reanalysis done in support of the final rule (i.e., an MIR of 100 in a million and an incidence of 0.55 cases/yr).

In the current assessment using the 1999 NEI data and the CalEPA URE for PCE, the risk distribution for the population showed that approximately 13,000,000 people (or about 7 percent of the total exposed population) have a risk equal to or greater than 1 in a million, with 300 people having a risk equal to or greater than 100 in a million (Exhibit 1a).  The assessment done at proposal (which also used the 1999 data) showed approximately 6,000,000 people (or about 3 percent of the total exposed population) with a risk equal to or greater than 1 in a million, with 100 of them having a risk estimated at equal to or greater than 100 in a million.  As expected, use of the newer residence time distribution resulted in an increase in the numbers of people in various risk bins greater than 1 in a million.  The population numbers in the current analysis seem to be consistently about 2 times larger than in the previous analysis.

A similar trend was seen when the population risk results using the 2002 NEI and the CalEPA URE for PCE are compared to that of the 1999 NEI (Exhibit 1a).  In the 2002 analysis, the residence time shift increased the number of people with a risk equal to or greater than 1 in a million from approximately 4,000,000 people to 8,000,000 people.  The MIR remained the same (100 in a million) as did the incidence (0.55 cases/yr).

The above discussion shows that the current risk assessment at the baseline level yields results that are comparable to baseline risk assessments done at proposal using the 1999 NEI or the reassessment using the 2002 NEI done to support the final rule.  As expected, the population numbers consistently show the increase in the numbers of people with a risk equal to or greater than 1 in a million while the MIR and incidence results agree with the previous assessments results.

3.2.	Risk Assessment Overall and by Industry Sector

One major difference between this current assessment and previous assessments done for the purposes of supporting the proposal or the final rule is that here we have evaluated cancer risk not only for the entire category but also separately for each industry sector.  This provides us a way to compare the risk contribution of each sector to risks seen across the entire source category.  The following sections present the result of each sector separately and, in addition, show the effect of applying the 40,000, 60,000, and 100,000 kg/yr emission levels across each sector and the effect of using the EPA’s Office of Prevention, Pesticides and Toxic Substances (OPPTS) URE for PCE.  The results presented in Exhibits 1a and 1b through 6a and 6b cover the uncontrolled and controlled emissions for all halogenated solvent cleaning facilities as well as those in the four industry sectors (aerospace, military depot, narrow tube, and continuous web cleaning) and a group of facilities referred to here as “other” that comprises all facilities left in the source category when the facilities in the four specific sectors are removed.  As a group, this latter collection of facilities (i.e., those identified as “other”) represents approximately 89 percent of all the identified facilities in the halogenated solvent cleaning source category regardless of inventory year.

3.2a.	Overall Category

As discussed above, this current reassessment estimated an MIR of 200 in a million with an incidence of 0.66 cases/yr when the 1999 NEI inventory is used with the CalEPA URE for PCE (Exhibit 1a).  There were approximately 13,000,000 people (or about 7 percent of the total exposed population) with a risk equal to or greater than 1 in a million and 300 people with a risk equal to or greater than 100 in a million.

The application of a 100,000 kg/yr emissions control to all facilities in this inventory decreased the MIR to 50 in a million and the incidence to 0.43 cases/yr (Exhibit 1b).  The more conservative control level of 60,000 kg/yr required by the final rule further decreased the MIR to 30 in a million, the incidence to 0.35 cases/yr, the number of people with a risk equal to or greater than 1 in a million to about 3,000,000 (or about 2 percent of the total exposed population), and the number of people with a risk equal to or greater than 100 in a million to 0 (Exhibit 1a).  The most conservative emissions control of 40,000 kg/yr produced an MIR of 20 in a million and an incidence of 0.28 cases/yr (Exhibit 1b).  As expected, use of the OPPTS URE for PCE resulted in further decreases in the MIR, incidence, and risk.

Because the 2002 NEI identified fewer facilities in the halogenated solvent cleaning inventory, and because of a corresponding decrease in inventory-total carcinogen emissions, it was expected that there would be a decrease in all estimated risk metrics.  As shown in Exhibit 1a with 2002 NEI, the MIR was 100 in a million (versus 200 in a million with 1999 data) with an incidence of 0.55 cases/yr (versus 0.66 cases/yr with 1999 data) using the CalEPA URE for PCE.  Approximately 8,000,000 people (or about 4 percent of the total exposed population) were exposed to a risk equal to or greater than 1 in a million (versus 13,000,000 people with 1999 data), and 100 people were exposed to a risk equal to or greater than 100 in a million (versus 300 people with 1999 data).

Using the 2002 data, the application of a 100,000 kg/yr emissions control to all facilities in this inventory decreased the MIR to 50 in a million and the incidence to 0.38 cases/yr (Exhibit 1b).  A 60,000 kg/yr control level decreased the MIR further to 30 in a million, the incidence to 0.32 cases/yr, and the number of people with a risk equal to or greater than 1 in a million to about 2,000,000 (or about 1 percent of the total exposed population) (Exhibit 1a). The most conservative emissions control of 40,000 kg/yr produced an MIR of 20 in a million and an incidence of 0.26 cases/yr (Exhibit 1b).  The use of the OPPTS URE for PCE with this inventory also resulted in further decreases in all estimated risk metrics.

3.2b.	Aerospace Sector

Aerospace sector risk results are presented in Exhibits 2a and 2b.  This sector comprised the largest of the four sectors considered separately in the final rule, and the 1999 NEI inventory identified only slightly more facilities than in the 2002 NEI (186 and 171 facilities, respectively, when scaled up).  At the baseline level and using the 1999 NEI inventory with the CalEPA URE for PCE, the sector MIR was estimated at 80 in a million with an incidence of 0.09 cases/yr (Exhibit 2a).  There were about 1,000,000 people (or about 2 percent of the total exposed population) with a risk equal to or greater than 1 in a million.  There were no individuals with a risk equal to or greater than 100 in a million.

When the 100,000 kg/yr control level was applied to this sector, the MIR decreased to 20 in a million, the incidence to 0.04 cases/yr, and the number of people with a risk equal to or greater than 1 in a million to about 300,000  (Exhibit 2b).  The 60,000 kg/yr control level also produced an MIR of 20 in a million, with an incidence of 0.04 cases/yr, and about 100,000 people (or less than 1 percent of the total exposed population) with a risk equal to or greater than 1 in a million (Exhibit 2a).  The most conservative control of 40,000 kg/yr also produced an MIR of 20 in a million, while reducing the incidence to 0.03 cases/yr (Exhibit 2b).

Use of the OPPTS URE for PCE produced lower risk metrics but the decreases were not as large as those seen for the entire source category.  In some cases (e.g., the MIR), there was no change in the metric value across control level or inventory year.

Using the 2002 NEI data, which was the inventory used to support the final rule, the incidence for this sector accounted for about 9 percent (0.05 out of 0.55 cases/yr) of the total incidence seen for the whole category.

3.2c.	Military Depot

Military depot sector risk results are presented in Exhibits 3a and 3b.  This sector was the smallest of all the sectors with only 3 and 5 facilities (when scaled up) identified in the 1999 and 2002 inventories, respectively.  The sector risks were also very low with an MIR of 6 in a million estimated for the 2002 NEI year (Exhibit 3a).  The corresponding incidence is low at 0.0005 cases/yr.  The maximum number of people shown to have a risk equal to or greater than 1 in a million was about 3,000 (or less than 1 percent of the total exposed population).  This occurred at the baseline level for the 2002 NEI, but no individuals had a risk level greater than 10 in a million.  The use of the OPPTS URE had no effect on these risk values since these facilities do not emit any PCE.

3.2d.	Narrow Tube

Narrow tube sector risk results are presented in Exhibits 4a and 4b.  As with the military depots sector, this sector has a small number of facilities identified in the two inventory databases (when scaled up, there were 16 and 25 carcinogen-emitting narrow tube facilities in the 1999 and 2002 NEI halogenated solvent cleaning datasets, respectively).  For the 1999 NEI using the CalEPA URE for PCE, the sector MIR was 30 in a million with an incidence of 0.03 cases/yr (Exhibit 4a).  Approximately 120,000 people (or about 1 percent of the total exposed population) had a risk equal to or greater than 1 in a million, with only about 400 of these having a risk between 10 in a million and 100 in a million.

When the 100,000 kg/yr control level was applied to these few facilities, the MIR remained at 30 in a million, the incidence decreased to 0.02 cases/yr, and about 75,000 people (or less than 1 percent of the total exposed population) had a risk equal to or greater than 1 in a million (Exhibit 4b).  The 60,000 kg/yr control level decreased the MIR to 20 in a million, the incidence to 0.01 cases/yr, and the number of people with a risk equal to or greater than 1 in a million to about 20,000 (or less than 1 percent of the total exposed population) (Exhibit 4a).  The most conservative emissions control of 40,000 kg/yr further reduced the MIR to 10 in a million, the incidence to 0.008 cases/yr, and the number of people with a risk equal to or greater than 1 in a million to about 17,000 (or less than 1 percent of the total exposed population) (Exhibit 4b).

Compared with the 1999 data, using the 2002 NEI with the CalEPA URE for PCE increased the sector MIR from 30 in a million to 50 in a million but decreased the incidence from 0.03 cases/yr to 0.02 cases/yr due to the fewer number of people with a risk equal to or greater than 1 in a million (i.e., about 90,000 people, or about 2% of the total exposed population) (Exhibit 4a).  This incidence contributed approximately 2 percent (0.01 out of 0.55 cases/yr) to the total incidence across the category.  The application of the 100,000 kg/yr control level decreased the MIR to 40 in a million, the incidence to 0.01 cases/yr, and the number of people with a risk equal to or greater than 1 in a million to about 54,000 (Exhibit 4b).  The 60,000 kg/yr control further decreased the sector MIR to 20 in a million, the incidence to 0.007 cases/yr, and the number of people with a risk equal to or greater than 1 in a million to about 16,000 (or less than 1 percent of the total exposed population) (Exhibit 4b).  The most conservative control level of 40,000 kg/yr also produced an MIR of 20 in a million, while further reducing the incidence to 0.005 cases/yr and the number of people with a risk equal to or greater than 1 in a million to about 12,000 (or less than 1 percent of the total exposed population) (Exhibit 4b).  Use of the OPPTS URE resulted in slight to no changes in the annual incidence numbers and in the numbers of people at different risk levels.

3.2e.	Continuous Web Cleaning

Continuous web cleaning (CWC) sector risk results are presented in Exhibits 5a and 5b.  As with the military depots and narrow tube sectors, this group is comprised of a small number of facilities (when scaled up, there were 16 and 14 carcinogen-emitting CWC facilities in the 1999 and 2002 NEI halogenated solvent cleaning datasets, respectively).  Using the 1999 NEI with the CalEPA URE for PCE, the sector MIR was 40 in a million with an incidence of about 0.03 cases/yr (Exhibit 5a).  The number of people with a risk equal to or greater than 1 in a million was about 140,000 (or about 1 percent of the total exposed population) with no individuals having a risk level above 100 in a million.  Capping these emissions at 100,000 kg/yr reduced the sector MIR of 20 in a million and the incidence to 0.02 cases/yr (Exhibit 5b).  Further capping these emissions at 60,000 kg/yr yielded a sector MIR of 10 in a million, an incidence of 0.01 cases/yr, and about 34,000 people (or less than 1 percent of the total exposed population) with a risk equal to or greater than 1 in a million (Exhibit 5a).  Lowering the emissions cap further to 40,000 kg/yr again produced an MIR of 10 in a million, lowered the incidence to 0.01 cases/yr, and lowered the number of people with a risk equal to or greater than 1 in a million to about 27,000 (or less than 1 percent of the total exposed population) (Exhibit 5b).

Use of the OPPTS URE with baseline emissions decreased the sector MIR from 40 in a million to 10 in a million, the incidence from 0.03 cases/yr to 0.005 cases/yr, and the population with a risk equal to or greater than 1 in a million from about 140,000 to about 9,000 people (or less than 1 percent of the total exposed population) (Exhibit 5a).

Compared with using the 1999 data, using the 2002 NEI data with the CalEPA URE for PCE reduced the sector MIR from 40 in a million to 30 in a million and maintained the incidence at 0.03 cases/yr (Exhibit 5a).  This contributed approximately 5 percent to the total incidence across the entire inventory of facilities.  The total number of people with a risk equal to or greater than 1 in a million was approximately 110,000 (or about 1 percent of the total exposed population) (Exhibit 5a).  Compared with using the 1999 NEI data, use of the 2002 NEI data with this sector had slight to no effect on values of maximum individual risk or annual cancer incidence at the 40,000, 60,000, and 100,000 kg/yr emissions control levels (Exhibits 5a and 5b). When the OPPTS URE was used, all risk metrics showed decreases, indicating that many facilities in this group use PCE in their cleaning operations.

3.2f.	All Facilities Not Included In One of the 4 Sectors (”Other Sector”)

The risk results for the halogenated solvent cleaning facilities not part of the above four sectors are presented in Exhibits 6a and 6b.  Using the 1999 NEI inventory with the CalEPA URE for PCE, the sector MIR was estimated to be 200 in a million with an incidence of approximately 0.52 cases/yr (Exhibit 6a).  About 11,000,000 people (or about 6 percent of the total exposed population) had a risk equal to or greater than 1 in a million, with 500 of these having a risk equal to or greater than 100 in a million.  Using the 100,000 kg/yr control level produced an MIR of 50 in a million with an incidence of 0.35 cases/yr (Exhibit 6b).  Capping these emissions at the 60,000 kg/yr level decreased the sector MIR to 30 in a million, the incidence to 0.29 cases/yr, and the total population with a risk equal to or greater than 1 in a million to approximately 2,500,000 (or about 1 percent of the total exposed population) (Exhibit 6a).   Capping these emissions further at 40,000 kg/yr further decreased the MIR to 20 in a million, the incidence to 0.23 cases/yr, and the total population with a risk equal to or greater than 1 in a million to approximately 1,703,000 (or about 1 percent of the total exposed population) (Exhibit 6b).

Compared to using the 1999 data, using the 2002 NEI with the CalEPA URE for PCE reduced the sector MIR from 200 in a million to 100 in a million and the incidence from 0.52 cases/yr to 0.45 cases/yr (Exhibit 6a).  This incidence level contributed approximately 82 percent to the total incidence estimated for the entire source category.  This is expected since this “sector” has approximately 89 percent of the facilities and includes about 93 percent of the total exposed population in the entire source category.  The total population with a risk equal to or greater than 1 in a million was approximately 7,000,000 people (or about 4 percent of the total exposed population), with about 70 people having a risk equal to or greater than 100 in a million.  The emissions cap of 100,000 kg/yr reduced the MIR to 50 in a million and the incidence to 0.31 cases/yr (Exhibit 6b).  When the emissions were capped at 60,000 kg/yr, the sector MIR was reduced to 30 in a million, the incidence to 0.26 cases/yr, and the population with a risk equal to or greater than 1 in a million to about 1,500,000 people (or about 1 percent of the total exposed population), with no individual having a risk equal to or greater than 100 in a million (Exhibit 6a).  Further capping the emissions at 40,000 kg/yr reduced the MIR to 20 in a million, the incidence to 0.22 cases/yr, and the population with a risk equal to or greater than 1 in a million to about 1,000,000 people (or about 1 percent of the total exposed population) (Exhibit 6b).  The use of the OPPTS URE did not affect the sector MIR but did reduce the cancer incidence and populations at various risk levels.

4. 	Discussion

This reassessment was intended to provide a risk assessment to support the 60,000 kg/yr emissions level required in the final rule.  This emission control level affects the majority of the facilities in this source category.  In addition, we performed separate risk assessments on the 4 industry sectors that had different requirements under the final halogenated solvent cleaning rule.  These latter analyses allow the EPA to see their specific contributions to the overall risk and help support the final rule requirements.  As an internal check on the modeling, we redid some assessments that were done previously.  This included the baseline level (i.e., no emission control) and the 40,000 kg/yr methylene chloride emissions control level using the 1999 National Emissions Inventory (NEI) and using the 2002 NEI.  We also tested a less conservative control level of 100,000 kg/yr.  The 1999 NEI was used to support the rule proposal in August, 2006.  The 2002 NEI was used to support the final rule published in May, 2007.  The other reason for redoing these earlier analyses was to determine the impact of using the updated residence time data and its shift to longer residence times.

In general, all risk metrics were higher using the 1999 NEI.  As stated before, this is due to the fact that there were more facilities identified in that database when compared with the 2002 NEI (i.e., 1,167 vs. 1,080) and the overall level of emissions was higher (i.e., approximately 9,800 t/yr vs. 6,500 t/yr, where t is English short tons).   When all the risk data, regardless of inventory year, were compared, it was evident that emissions from facilities in the Aerospace sector and the group of facilities called “other” were the major contributors to the overall cancer incidence.  Specifically, of the total annual cancer incidence level of 0.55 cases/yr across the entire source category (2002 NEI, CalEPA PCE URE, baseline emissions), emissions from the Aerospace sector contributed approximately 9 percent while those from the “other” group contributed approximately 82 percent.  The remaining sectors combined (i.e., military depot, narrow tube, and continuous web cleaning) contributed about 10 percent.

Given the uncertainties associated with the development of emission inventories, neither the 1999 nor the 2002 NEI inventory should be considered accurate in an absolute sense, and the difference between the two inventories should not necessarily be interpreted as temporal trends in degreasing machine populations or emissions.  Rather, we consider them to be “snapshots” of the true long-term inventory of emissions for this source category, each carrying its own degree of uncertainty.  As such, the derived risk assessment results should be regarded as ranges within which the true risk metrics are likely to exist.

Exhibit 1a

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, CalEPA and OPPTS UREs, and baseline and 60,000 kg/yr controls: Scaled to National Level
 All Halogenated Solvent Cleaning Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | OPPTS PCE URE 3 | CalEPA PCE URE 3 | OPPTS PCE URE 3 |
|  | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 200 | 30 | 90 | 20 | 100 | 30 | 100 | 30 |
| Estimated annual cancer incidence 2 | 0.66 | 0.35 | 0.26 | 0.22 | 0.55 | 0.32 | 0.25 | 0.20 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 300 | 0 | 0 | 0 | 100 | 0 | 20 | 0 |
| ≥ 10 to < 100 | 120,000 | 5,000 | 13,000 | 1,000 | 82,000 | 4,000 | 9,000 | 800 |
| ≥ 1 to < 10 | 13,000,000 | 3,300,000 | 2,000,000 | 1,200,000 | 8,000,000 | 2,000,000 | 1,600,000 | 860,000 |
| Total Pop ≥ 1 | 13,120,300 | 3,305,000 | 2,013,000 | 1,201,000 | 8,082,100 | 2,004,000 | 1,609,020 | 860,800 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 7 | 0 | 0 | 0 | 9 | 0 | 2 | 0 |
| ≥ 10 to < 100 | 114 | 50 | 72 | 30 | 86 | 51 | 51 | 26 |
| ≥ 1 to < 10 | 423 | 488 | 374 | 415 | 394 | 438 | 352 | 378 |
| < 1 (only carcinogen emitters) | 666 | 672 | 764 | 765 | 802 | 802 | 886 | 887 |
| < 1 (including sources emitting non-carcinogens) 4 | 1,356 | 1,362 | 1,454 | 1,455 | 1,411 | 1,411 | 1,495 | 1,496 |
| All facilities 5 | 1,900 | 1,900 | 1,900 | 1,900 | 1,900 | 1,900 | 1,900 | 1,900 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1; OPPTS URE for PCE= 7.1 x 10-7 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 690 (424 scaled up) of the Year 1999 facilities and 609 (346 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). |

Exhibit 1b

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, only CalEPA URE, and 40,000 kg/yr and 100,000 kg/yr controls: Scaled to National Level
 All Halogenated Solvent Cleaning Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | CalEPA PCE URE 3 |
|  | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 20 | 50 | 20 | 50 |
| Estimated annual cancer incidence 2 | 0.28 | 0.43 | 0.26 | 0.38 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | Not Generated | Not Generated | Not Generated | Not Generated |
| ≥ 10 to < 100 | Not Generated | Not Generated | Not Generated | Not Generated |
| ≥ 1 to < 10 | Not Generated | Not Generated | Not Generated | Not Generated |
| Total Pop ≥ 1 | Not Generated | Not Generated | Not Generated | Not Generated |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 28 | 83 | 17 | 74 |
| ≥ 1 to < 10 | 506 | 459 | 468 | 415 |
| < 1 (only carcinogen emitters) | 676 | 668 | 806 | 802 |
| < 1 (including sources emitting non-carcinogens) 4 | 1,366 | 1,358 | 1,415 | 1,411 |
| All facilities 5 | 1,900 | 1,900 | 1,900 | 1,900 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 690 (424 scaled up) of the Year 1999 facilities and 609 (346 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). |

Exhibit 2a

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, CalEPA and OPPTS UREs, and baseline and 60,000 kg/yr controls: Scaled to National Level
 Aerospace Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | OPPTS PCE URE 3 | CalEPA PCE URE 3 | OPPTS PCE URE 3 |
|  | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 80 | 20 | 20 | 20 | 30 | 20 | 30 | 20 |
| Estimated annual cancer incidence 2 | 0.09 | 0.04 | 0.03 | 0.02 | 0.05 | 0.03 | 0.02 | 0.01 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 24,000 | 500 | 400 | 100 | 3,000 | 100 | 200 | 30 |
| ≥ 1 to < 10 | 990,000 | 100,000 | 120,000 | 25,000 | 360,000 | 63,000 | 79,000 | 22,000 |
| Total Pop ≥ 1 | 1,014,000 | 100,500 | 120,400 | 25,100 | 363,000 | 63,100 | 79,200 | 22,030 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 16 | 10 | 5 | 5 | 14 | 9 | 4 | 4 |
| ≥ 1 to < 10 | 38 | 42 | 26 | 26 | 23 | 28 | 21 | 21 |
| < 1 (only carcinogen emitters) | 54 | 56 | 77 | 77 | 81 | 81 | 93 | 93 |
| < 1 (including sources emitting non-carcinogens) 4 | 132 | 134 | 155 | 155 | 134 | 134 | 146 | 146 |
| All facilities 5 | 186 | 186 | 186 | 186 | 171 | 171 | 171 | 171 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1; OPPTS URE for PCE= 7.1 x 10-7 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 78 (48 scaled up) of the Year 1999 facilities and 53 (30 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). |

Exhibit 2b

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, only CalEPA URE, and 40,000 kg/yr and 100,000 kg/yr controls: Scaled to National Level
 Aerospace Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | CalEPA PCE URE 3 |
|  | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 20 | 20 | 20 | 30 |
| Estimated annual cancer incidence 2 | 0.03 | 0.04 | 0.02 | 0.04 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | Not Generated | 06 | Not Generated | 06 |
| ≥ 10 to < 100 | Not Generated | 2,5006 | Not Generated | 2,0006 |
| ≥ 1 to < 10 | Not Generated | 300,0006 | Not Generated | 300,0006 |
| Total Pop ≥ 1 | Not Generated | 302,5006 | Not Generated | 302,0006 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 5 | 10 | 5 | 9 |
| ≥ 1 to < 10 | 44 | 42 | 30 | 28 |
| < 1 (only carcinogen emitters) | 59 | 56 | 83 | 81 |
| < 1 (including sources emitting non-carcinogens) 4 | 137 | 134 | 136 | 134 |
| All facilities 5 | 186 | 186 | 171 | 171 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 78 (48 scaled up) of the Year 1999 facilities and 53 (30 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). 6 Population numbers were interpolated. |

Exhibit 3a

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, CalEPA and OPPTS UREs, and baseline and 60,000 kg/yr controls: Scaled to National Level 
 Military Depot Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | OPPTS PCE URE 3 | CalEPA PCE URE 3 | OPPTS PCE URE 3 |
|  | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 3 | 2 | 3 | 2 | 6 | 2 | 6 | 2 |
| Estimated annual cancer incidence 2 | 0.0002 | 0.0002 | 0.0002 | 0.0002 | 0.0005 | 0.0002 | 0.0005 | 0.0002 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 1 to < 10 | 700 | 200 | 700 | 200 | 3,000 | 200 | 3,000 | 200 |
| Total Pop ≥ 1 | 700 | 200 | 700 | 200 | 3,000 | 200 | 3,000 | 200 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 1 to < 10 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| < 1 (only carcinogen emitters) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
| < 1 (including sources emitting non-carcinogens) 4 | 1 | 1 | 1 | 1 | 3 | 3 | 3 | 3 |
| All facilities 5 | 3 | 3 | 3 | 3 | 5 | 5 | 5 | 5 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1; OPPTS URE for PCE= 7.1 x 10-7 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 0 of the Year 1999 facilities and 2 (1 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). |

Exhibit 3b

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, only CalEPA URE, and 40,000 kg/yr and 100,000 kg/yr controls: Scaled to National Level 
 Military Depot Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | CalEPA PCE URE 3 |
|  | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 1 | 3 | 1 | 3 |
| Estimated annual cancer incidence 2 | 0.0001 | 0.0002 | 0.0001 | 0.0002 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | Not Generated | 0 | Not Generated | 0 |
| ≥ 10 to < 100 | Not Generated | 0 | Not Generated | 0 |
| ≥ 1 to < 10 | Not Generated | 4006 | Not Generated | 1,5006 |
| Total Pop ≥ 1 | Not Generated | 4006 | Not Generated | 1,5006 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 0 | 0 | 0 | 0 |
| ≥ 1 to < 10 | 2 | 2 | 2 | 2 |
| < 1 (only carcinogen emitters) | 1 | 1 | 1 | 1 |
| < 1 (including sources emitting non-carcinogens) 4 | 1 | 1 | 3 | 3 |
| All facilities 5 | 3 | 3 | 5 | 5 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 0 of the Year 1999 facilities and 2 (1 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). 6 Population numbers were interpolated. |

Exhibit 4a

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, CalEPA and OPPTS UREs, and baseline and 60,000 kg/yr controls: Scaled to National Level 
 Narrow Tube Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | OPPTS PCE URE 3 | CalEPA PCE URE 3 | OPPTS PCE URE 3 |
|  | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 30 | 20 | 30 | 20 | 50 | 20 | 50 | 20 |
| Estimated annual cancer incidence 2 | 0.03 | 0.01 | 0.01 | 0.009 | 0.02 | 0.007 | 0.02 | 0.007 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 400 | 80 | 400 | 70 | 1,000 | 100 | 1,000 | 100 |
| ≥ 1 to < 10 | 120,000 | 23,000 | 44,000 | 20,000 | 89,000 | 16,000 | 89,000 | 16,000 |
| Total Pop ≥ 1 | 120,400 | 23,080 | 44,400 | 20,070 | 90,000 | 16,100 | 90,000 | 16,100 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 10 | 2 | 8 | 2 | 14 | 5 | 14 | 5 |
| ≥ 1 to < 10 | 5 | 13 | 6 | 13 | 9 | 18 | 9 | 18 |
| < 1 (only carcinogen emitters) | 1 | 1 | 2 | 1 | 2 | 2 | 2 | 2 |
| < 1 (including sources emitting non-carcinogens) 4 | 1 | 1 | 2 | 1 | 2 | 2 | 2 | 2 |
| All facilities 5 | 16 | 16 | 16 | 16 | 25 | 25 | 25 | 25 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1; OPPTS URE for PCE= 7.1 x 10-7 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 0 of the Year 1999 facilities and 0 of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). |

Exhibit 4b

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, only CalEPA URE, and 40,000 kg/yr and 100,000 kg/yr controls: Scaled to National Level 
 Narrow Tube Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | CalEPA PCE URE 3 |
|  | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 10 | 30 | 10 | 40 |
| Estimated annual cancer incidence 2 | 0.008 | 0.02 | 0.005 | 0.01 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 06 | 06 | 06 | 06 |
| ≥ 10 to < 100 | 606 | 3006 | 706 | 7006 |
| ≥ 1 to < 10 | 17,0006 | 75,0006 | 12,0006 | 53,0006 |
| Total Pop ≥ 1 | 17,0606 | 75,3006 | 12,0706 | 53,7006 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 2 | 5 | 2 | 9 |
| ≥ 1 to < 10 | 13 | 10 | 21 | 14 |
| < 1 (only carcinogen emitters) | 1 | 1 | 2 | 2 |
| < 1 (including sources emitting non-carcinogens) 4 | 1 | 1 | 2 | 2 |
| All facilities 5 | 16 | 16 | 25 | 25 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 0 of the Year 1999 facilities and 0 of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). 6 Population numbers were interpolated. |

Exhibit 5a

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, CalEPA and OPPTS UREs, and baseline and 60,000 kg/yr controls: Scaled to National Level 
 Continuous Web Cleaning Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | OPPTS PCE URE 3 | CalEPA PCE URE 3 | OPPTS PCE URE 3 |
|  | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 40 | 10 | 10 | 10 | 30 | 10 | 9 | 9 |
| Estimated annual cancer incidence 2 | 0.03 | 0.01 | 0.005 | 0.004 | 0.03 | 0.02 | 0.005 | 0.004 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 2,000 | 20 | 80 | 20 | 500 | 100 | 0 | 0 |
| ≥ 1 to < 10 | 137,000 | 34,000 | 9,000 | 6,000 | 110,000 | 29,000 | 7,000 | 6,000 |
| Total Pop ≥ 1 | 139,000 | 34,020 | 9,080 | 6,020 | 110,500 | 29,100 | 7,000 | 6,000 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 9 | 1 | 3 | 2 | 5 | 3 | 0 | 0 |
| ≥ 1 to < 10 | 5 | 13 | 10 | 11 | 7 | 9 | 10 | 10 |
| < 1 (only carcinogen emitters) | 0 | 0 | 1 | 1 | 0 | 0 | 2 | 2 |
| < 1 (including sources emitting non-carcinogens) 4 | 2 | 2 | 3 | 3 | 2 | 2 | 4 | 4 |
| All facilities 5 | 16 | 16 | 16 | 16 | 14 | 14 | 14 | 14 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1; OPPTS URE for PCE= 7.1 x 10-7 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 2 (1 scaled up) of the Year 1999 facilities and 2 (1 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). |

Exhibit 5b

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, only CalEPA URE, and 40,000 kg/yr and 100,000 kg/yr controls: Scaled to National Level 
 Continuous Web Cleaning Facilities

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | CalEPA PCE URE 3 |
|  | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 10 | 20 | 8 | 20 |
| Estimated annual cancer incidence 2 | 0.01 | 0.02 | 0.01 | 0.02 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 06 | Not Generated | 06 | Not Generated |
| ≥ 10 to < 100 | 206 | Not Generated | 806 | Not Generated |
| ≥ 1 to < 10 | 27,0006 | Not Generated | 23,0006 | Not Generated |
| Total Pop ≥ 1 | 27,0206 | Not Generated | 23,0806 | Not Generated |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 0 | 5 | 0 | 3 |
| ≥ 1 to < 10 | 14 | 9 | 12 | 9 |
| < 1 (only carcinogen emitters) | 0 | 0 | 0 | 0 |
| < 1 (including sources emitting non-carcinogens) 4 | 2 | 2 | 2 | 2 |
| All facilities 5 | 16 | 16 | 14 | 14 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 2 (1 scaled up) of the Year 1999 facilities and 2 (1 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). 6 Population numbers were interpolated. |

Exhibit 6a

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, CalEPA and OPPTS UREs, and baseline and 60,000 kg/yr controls: Scaled to National Level
 Halogenated Solvent Cleaning Facilities Not in One of the 4 Sectors (All Other Facilities)

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | OPPTS PCE URE 3 | CalEPA PCE URE 3 | OPPTS PCE URE 3 |
|  | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions | Baseline no control | 60,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 200 | 30 | 90 | 20 | 100 | 30 | 100 | 30 |
| Estimated annual cancer incidence 2 | 0.52 | 0.29 | 0.22 | 0.19 | 0.45 | 0.26 | 0.21 | 0.18 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 500 | 0 | 0 | 0 | 71 | 0 | 21 | 0 |
| ≥ 10 to < 100 | 100,000 | 4,000 | 12,000 | 1,000 | 86,000 | 3,000 | 6,000 | 600 |
| ≥ 1 to < 10 | 11,000,000 | 2,600,000 | 1,800,000 | 1,100,000 | 7,000,000 | 1,600,000 | 1,200,000 | 760,000 |
| Total Pop ≥ 1 | 11,100,500 | 2,604,000 | 1,812,000 | 1,101,000 | 7,086,071 | 1,603,000 | 1,206,021 | 760,600 |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 7 | 0 | 0 | 0 | 9 | 0 | 2 | 0 |
| ≥ 10 to < 100 | 78 | 38 | 55 | 23 | 53 | 33 | 33 | 18 |
| ≥ 1 to < 10 | 374 | 418 | 331 | 361 | 353 | 382 | 310 | 327 |
| < 1 (only carcinogen emitters) | 609 | 612 | 682 | 684 | 718 | 718 | 788 | 788 |
| < 1 (including sources emitting non-carcinogens) 4 | 1,220 | 1,223 | 1,293 | 1,295 | 1,270 | 1,270 | 1,340 | 1,340 |
| All facilities 5 | 1,679 | 1,679 | 1,679 | 1,679 | 1,685 | 1,685 | 1,685 | 1,685 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1; OPPTS URE for PCE= 7.1 x 10-7 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 611 (375 scaled up) of the Year 1999 facilities and 552 (314 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). |

Exhibit 6b

Estimated Cancer Risk, Population Risk Distribution, and Estimated Number of Facilities at Various Risk Levels -- Using NEI 1999 and NEI 2002 Data, only CalEPA URE, and 40,000 kg/yr and 100,000 kg/yr controls: Scaled to National Level
 Halogenated Solvent Cleaning Facilities Not in One of the 4 Sectors (All Other Facilities)

| Cancer Risk Results | 1999 | 2002 |
| --- | --- | --- |
|  | CalEPA PCE URE 3 | CalEPA PCE URE 3 |
|  | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions | 40,000 kg/yr control cap on MC equiv emissions | 100,000 kg/yr control cap on MC equiv emissions |
| Estimated maximum individual lifetime cancer risk (per million) 1 | 20 | 50 | 20 | 50 |
| Estimated annual cancer incidence 2 | 0.23 | 0.35 | 0.22 | 0.31 |
| Estimated lifetime cancer risk (per million) | Estimated National Population |
| ≥ 100 | 06 | Not Generated | 06 | Not Generated |
| ≥ 10 to < 100 | 2,7006 | Not Generated | 2,0006 | Not Generated |
| ≥ 1 to < 10 | 1,700,0006 | Not Generated | 1,000,0006 | Not Generated |
| Total Pop ≥ 1 | 1,702,7006 | Not Generated | 1,002,0006 | Not Generated |
| Estimated lifetime cancer risk (per million) | Number of Facilities |
| ≥ 100 | 0 | 0 | 0 | 0 |
| ≥ 10 to < 100 | 21 | 63 | 11 | 53 |
| ≥ 1 to < 10 | 433 | 396 | 403 | 362 |
| < 1 (only carcinogen emitters) | 614 | 609 | 719 | 718 |
| < 1 (including sources emitting non-carcinogens) 4 | 1,225 | 1,220 | 1,271 | 1,270 |
| All facilities 5 | 1,679 | 1,679 | 1,685 | 1,685 |
| 1 Estimated maximum individual lifetime cancer risks are rounded to one significant figure. 2 Estimated annual cancer incidence and population counts have been rounded to two or three significant figures where appropriate. 3 CalEPA URE for PCE = 5.9 x 10-6 (ug/m3)-1. 4 Includes facilities with cancer risk < 1 plus 611 (375 scaled up) of the Year 1999 facilities and 552 (314 scaled up) of the Year 2002 facilities that emit only the non-carcinogen 1,1,1-trichloroethane (TCA). 5 Represents the total number of facilities in this category. This facility count should equal the sum of facilities with any maximum individual risk greater than or equal to 1 and the number of facilities with less than 1 (including sources emitting non-carcinogens). 6 Population numbers were interpolated. |

Appendix A

Probabilistic Analysis Methodology

In previous air toxics assessments, EPA used residence time estimates from the EPA Exposure Factors Handbook (1996).  These estimates were based on an analysis by Johnson and Capel (1992).  This analysis has two shortcomings that currently limit its usefulness for residual risk assessments.  First, the underlying data were from 1987.  Second, the approach was based on one-year move rates that appear to have underestimated residence time for long-term residents, as reported by the US Census Bureau in its Surveys of Income and Program Participation (SIPP, 1996 and 2001).

At EPA’s request, Ted Johnson (one of the original authors) updated the Johnson and Capel (1992) analysis to reflect the more recent SIPP data and a newer, more complete modeling approach.  Johnson’s model randomly selected subjects from the US Census Bureau’s American Community Survey database, and estimated time already spent in the residence, future time to be spent in the residence, and future length of life.  These estimates were combined to predict the total time, past and future, that the subject would occupy the current residence.  Johnson then compared the modeling results with SIPP residence time data and adjusted the results to compensate for “residential inertia” (i.e., a tendency in the SIPP data for long-term residents to have lower-than-expected move rates).  EPA is in the process of updating the Exposure Factors Handbook, and expects to replace its current residence time recommendations (Exhibit A-1, below) with Johnson’s new estimates (Exhibit A-2).  However, the entire Handbook must undergo scientific review, and EPA is not certain when that process will be complete.  For that reason, EPA has had these data reviewed by experts within the Office of Research and Development.  Their basic comment supported EPA’s thoughts that these data were an improvement over the previous data and that they should be used in this assessment.  The peer reviewer’s comments may be found in the docket for this rule.

Exhibit A-1

Residence time estimates (in years) from Johnson and Capel (1992).

| From | To | Probability |
| --- | --- | --- |
| 0 | 1.5 | 0.05 |
| 1.5 | 2.5 | 0.05 |
| 2.5 | 3.5 | 0.15 |
| 3.5 | 9 | 0.25 |
| 9 | 16 | 0.25 |
| 16 | 26 | 0.15 |
| 26 | 33 | 0.05 |
| 33 | 41 | 0.03 |
| 41 | 47 | 0.01 |
| 47 | 51 | 0.005 |
| 51 | 55 | 0.003 |
| 55 | 59 | 0.001 |
| 59 | 85 | 0.001 |

Exhibit A-2

Revised residence time estimates (in years) described above.

| From | To | Probability |
| --- | --- | --- |
| 0 | 1 | 0.05 |
| 1 | 2 | 0.05 |
| 2 | 5 | 0.15 |
| 5 | 12.6 | 0.25 |
| 12.6 | 27.2 | 0.25 |
| 27.2 | 45.6 | 0.15 |
| 45.6 | 56.3 | 0.05 |
| 56.3 | 74.9 | 0.04 |
| 74.9 | 81 | 0.005 |
| 81 | 91 | 0.004 |
| 91 | 100 | 0.001 |

Appendix B

Halogenated Solvent Cleaning Source Category Data from

1999 and 2002 National Emissions Inventory

Exhibit B-1

Selected Fields from the 1999 National Emissions Inventory Data for All Halogenated Solvent Cleaning Facilities

| Modeling ID | Secondary ID | Lat | Lon | Facility Name | City, State | Chemicals | MC Emission Rate (kg/yr)1 | PCE Emission Rate (kg/yr) 1 | TCA Emission Rate (kg/yr) 1 | TCE Emission Rate (kg/yr) 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2-1 |  | 42.929846 | -76.574253 | Auburn Technology | Auburn, NY | TCE |  |  |  | 511.4 |
| 3-1 |  | 43.109616 | -76.154395 | B.G. Sulzle | North Syracuse, NY | TCE |  |  |  | 3354.6 |
| 4-1 |  | 43.11582 | -77.48916 | Brainerd | East Rochester, NY | TCE |  |  |  | 1746.3 |
| 6-1 |  | 40.722256 | -73.948567 | Carter Spray Finishing | Brooklyn, NY | TCE |  |  |  | 3146.1 |
| 8-1 |  | 40.861035 | -73.15728 | Dover Findings | Saint James, NY | TCE |  |  |  | 97.2 |
| 12-1 |  | 43.054355 | -75.85809 | Gary-Syracuse | Chittenango, NY | TCA |  |  | 226.8 |  |
| 14-1 |  | 40.81562 | -73.426542 | Hitemco Div. Of Barson Composites | Old Bethpage, NY | TCE |  |  |  | 1014.3 |
| 16-1 |  | 43.093317 | -75.259719 | Indium Corp of America | Utica, NY | MC | 2392.9 |  |  |  |
| 19-1 |  | 42.0478 | -79.13159 | Keywell LLC | Frewsburg, NY | TCE |  |  |  | 2702.0 |
| 22-1 |  | 41.21177 | -73.98672 | Lighting Services Inc | Stony Point, NY | TCE |  |  |  | 6397.5 |
| 31-2 | NTI12930 | 35.42838 | -97.40599 | DOD - Tinker AFB |  | PCE |  | 7999.9 |  |  |
| 31-3 |  | 29.373462 | -98.549114 | DOD - Kelly AFB | Kelly AFB, TX | PCE |  | 7161.1 |  |  |
| 31-5 |  | 47.56357 | -122.62704 | DOD - Puget Sound Naval Shipyard | Bremerton, WA | TCE |  |  |  | 667.8 |
| 36-1 |  | 34.219326 | -92.006093 | Central Moloney | Pine Bluff, AK | PCE |  | 53336.9 |  |  |
| 37-1 |  | 35.472203 | -93.473792 | Greenville Tube | Clarksville, AR | TCE |  |  |  | 64878.7 |
| 38-1 |  | 35.056563 | -106.553858 | DOE - Sandia NL | Albuquerque, NM | PCE,TCE |  | 27.2 |  | 157.0 |
| 39-1 |  | 36.209014 | -95.868265 | American Airlines | Tulsa, OK | PCE,TCE |  | 29458.3 |  | 11614.4 |
| 40-4 |  | 47.311497 | -122.363224 | Boeing Defense | Kent, WA | PCE,TCE |  | 1999.2 |  | 5617.5 |
| 42-1 | NTI12973 | 36.176958 | -95.850958 | Nordam Repair Div. | Tulsa, OK | TCE |  |  |  | 4028.2 |
| 44-1 |  | 32.82127 | -96.842767 | Dallas Airmotive | Dallas, TX | TCE |  |  |  | 1527.3 |
| 45-1 |  | 32.94808 | -96.834807 | Dallas Semiconductor | Dallas, TX | MC | 1257.4 |  |  |  |
| 49-1 |  | 33.18694 | -96.29664 | J&S Plating and Repair | Farmersville, TX | TCE |  |  |  | 917.7 |
| 53-1 |  | 32.74706 | -96.89867 | Northrop Gruman | Dallas, TX | PCE |  | 1044.0 |  |  |
| 54-1 |  | 29.9024 | -97.95026 | Parkview Metal Products | San Marcos, TX | TCE |  |  |  | 24207.3 |
| 56-1 |  | 32.75448 | -98.900853 | R.E. Dye Manufacturing | Breckenridge, TX | TCE |  |  |  | 741.5 |
| 57-2 | NTITXRDF0558 | 33.004 | -97.3102 | Texas Aero engine Service | Forth Worth, TX | TCE |  |  |  | 2094.1 |
| 59-1 |  | 32.44746 | -99.6942 | U.S. Brass | Abilene, TX | TCE |  |  |  | 2988.2 |
| 60-1 |  | 32.407893 | -99.724832 | Victor Equipment | Abilene, TX | TCE |  |  |  | 7146.0 |
| 61-1 | NTITXT$11144 | 32.953502 | -96.886172 | Wolverine Tube - Tube Forming, Inc. | Carrollton, TX | TCE |  |  |  | 15022.1 |
| 73-1 |  | 30.38 | -89.6 | Stennis space center |  | TCA |  |  | 818.4 |  |
| 75-1 |  |  |  | A.O. SMITH/UPPCO | MONTICELLO, IN | TCE |  |  |  | 67.6 |
| 78-1 |  | 41.6941 | -85.88828 | AUSPRO MFG. CO. | ELKHART, IN | TCE |  |  |  | 349.3 |
| 79-1 |  | 38.3536 | -87.3246 | BRIDON AMERICAN CORP. | OAKLAND CITY, IN | TCA |  |  | 220.6 |  |
| 80-1 |  | 39.18311 | -85.89459 | CALFLEX | COLUMBUS, IN | TCE |  |  |  | 446.3 |
| 81-1 |  | 39.76727 | -86.1117 | CMW, INC. | INDIANAPOLIS, IN | TCE |  |  |  | 7439.0 |
| 82-1 |  | 39.76306 | -86.13889 | COMMERCIAL PLATING CO., INC. | INDIANAPOLIS, IN | PCE |  | 302.6 |  |  |
| 83-1 |  |  |  | CORE TECH | WARSAW, IN | TCE |  |  |  | 1152.6 |
| 84-1 |  | 37.97018 | -87.54258 | CRADDOCK FINISHING CORP. | EVANSVILLE, IN | TCE |  |  |  | 792.1 |
| 85-1 |  | 40.45558 | -86.10348 | CRAFTSMAN COATING, CO. | EVANSVILLE, IN | TCE |  |  |  | 78.0 |
| 86-2 |  | 40.76565 | -86.05912 | DELPHI DELCO ELECTRONICS SYSTEMS | KOKOMO, IN | TCE |  |  |  | 3667.3 |
| 87-1 |  | 41.35056 | -85.14686 | DOUGLASS ELECTRIC MOTOR REPAIR | PERU, IN | TCE |  |  |  | 193.7 |
| 88-1 |  | 41.35056 | -85.1433 | ELECTRIC MOTORS & SPECIALTIES, INC. | GARRETT, IN | MC | 35.5 |  |  |  |
| 90-1 |  |  |  | ELKHART PRODUCTS | GENEVA, IN | TCE |  |  |  | 1003.2 |
| 91-1 |  | 39.92104 | -86.25991 | ELLIOTT COMPANY OF INDIANAPOLIS | INDIANAPOLIS, IN | TCE |  |  |  | 17.2 |
| 92-1 |  |  |  | ELSA CORPORATION | ELWOOD, IN | TCE |  |  |  | 3087.9 |
| 93-1 |  | 41.68044 | -85.91992 | F&F SCREW MACHINE PRODUCTS, INC. | ELKHART, IN | TCE |  |  |  | 553.2 |
| 94-1 |  | 39.552 | -86.3699 | FEDERAL-MOGUL, CORP. | MOORESVILLE, IN | TCE |  |  |  | 873.2 |
| 95-1 |  | 39.64805 | -85.13872 | FORD ELECTRONICS & REFRIGERATION | CONNERSVILLE, IN | TCE |  |  |  | 20457.1 |
| 97-1 |  | 40.82483 | -84.9414 | GILPIN IRONWORKS | DECATUR, IN | TCE |  |  |  | 11315.7 |
| 98-1 |  |  |  | HAND INDUSTRIES, INC. | WARSAW, IN | TCE |  |  |  | 572.8 |
| 99-1 |  | 38.34678 | -87.57276 | HANSEN CORPORATION | PRINCETON, IN | TCE |  |  |  | 148.8 |
| 100-1 |  | 38.36171 | -85.81399 | HITACHI CABLE INDIANA, INC. | NEW ALBANY, IN | TCE |  |  |  | 4191.2 |
| 101-1 |  | 41.3537 | -86.33384 | HOOSIER TIRE AND RUBBER | PLYMOUTH, IN | MC | 232.3 |  |  |  |
| 102-1 |  | 39.76722 | -86.13329 | HORNER ELECTRIC INC. | INDIANAPOLIS, IN | TCE |  |  |  | 5597.7 |
| 104-1 |  |  |  | IDX, INC. | MCCORDSVILLE, IN | TCE |  |  |  | 122.2 |
| 105-1 |  | 39.128 | -85.964 | INDIANA METAL COATINGS, INC. | COLUMBUS, IN | MC | 32655.9 |  |  |  |
| 106-1 |  | 38.36953 | -86.94266 | JASPER ENGINE EXCHANGE, INC. | JASPER, IN | MC | 2129.3 |  |  |  |
| 107-1 |  | 38.2923 | -85.7985 | K AND I HARD CHROME, INC. | NEW ALBANY, IN | TCE |  |  |  | 371.9 |
| 108-1 |  | 39.52178 | -85.7892 | K.C.L. CORP. | SHELBYVILLE, IN | PCE |  | 1894.3 |  |  |
| 109-1 |  | 39.7536 | -86.10324 | KECO ENGINEERED COATINGS, INC. | INDIANAPOLIS, IN | TCE |  |  |  | 3457.8 |
| 110-1 |  | 40.85937 | -85.52842 | KEN-KOAT, INC. | HUNTINGTON, IN | TCA |  |  | 2603.6 |  |
| 111-1 |  | 39.87619 | -86.08323 | K-T CORP | SHELBYVILLE, IN | TCE |  |  |  | 18225.4 |
| 112-1 |  | 41.08598 | -85.23638 | LINCOLN FOODSERVICE PRODUCTS | FORT WAYNE, IN | TCE |  |  |  | 67911.3 |
| 113-1 |  |  |  | MACHINE-RITE PRODUCTS | LAGRANGE, IN | TCE |  |  |  | 2975.6 |
| 114-1 |  | 41.68952 | -85.94523 | MCDOWELL ENTERPRISES, INC. | ELKHART, IN | TCE |  |  |  | 4798.1 |
| 115-1 |  | 38.3434 | -87.5629 | MID STATES RUBBER | PRINCETON, IN | PCE |  | 14877.9 |  |  |
| 116-1 |  | 40.87928 | -85.17819 | MONARCH SPECIALTY SYSTEMS, INC. | OSSIAN, IN | TCE |  |  |  | 327.3 |
| 117-1 |  | 39.70691 | -86.3899 | OAK-RITE MFG. CORP. | PLAINFIELD, IN | TCE |  |  |  | 4418.7 |
| 118-1 |  | 41.6823 | -85.92558 | PETTIFOR'S, INC. | ELKHART, IN | TCE |  |  |  | 23.3 |
| 119-1 |  | 41.08006 | -85.16911 | PRECISIONEERING, INC. | FT. WAYNE, IN | TCA |  |  | 307.4 |  |
| 121-1 |  | 40.00446 | -86.8854 | RAYBESTOS PRODUCTS, CO. | CRAWFORDSVILLE, IN | TCE |  |  |  | 57557.4 |
| 122-1 |  | 38.3422 | -85.8325 | REDI STRIP OF NEW ALBANY, INC. | NEW ALBANY, IN | MC | 10065.6 |  |  |  |
| 123-1 |  | 41.65697 | -86.16718 | REMOTE CONTROLS, INC. | MISHAWAKA, IN | TCE |  |  |  | 2257.0 |
| 124-1 |  | 41.66297 | -86.23143 | SOUTH BEND CONTROLS, INC. | SOUTH BEND, IN | TCE |  |  |  | 5343.8 |
| 125-1 |  | 41.68557 | -85.93449 | THE SELMER COMPANY/VINCENT BACH DIV. | ELKHART, IN | TCE |  |  |  | 54657.2 |
| 129-1 |  | 43.392452 | -123.294779 | Caddock | Roseburg, OR | PCE |  | 325.9 |  |  |
| 130-1 |  | 47.662414 | -122.372221 | Color Tech Division of ASKO | Seattle, OR | TCE |  |  |  | 1306.0 |
| 130-2 |  |  |  |  |  | TCE |  |  |  | 1834.7 |
| 133-1 |  | 45.487802 | -122.638376 | Electro-Chem Metal Finishing | Portland, OR | TCE |  |  |  | 922.1 |
| 141-1 |  | 45.60283 | -122.67277 | Portland Public School | Portland, OR | TCA |  |  | 208.7 |  |
| 144-1 |  | 45.49932 | -122.810161 | Tektronix | Beaverton, OR | TCE |  |  |  | 220.8 |
| 145-1 |  | 45.498344 | -122.814477 | Vispro | Beaverton, OR | TCE |  |  |  | 642.8 |
| 147-1 |  | 47.553462 | -122.329635 | Art Brass Plating, Inc. | Seattle, WA | TCE |  |  |  | 2533.5 |
| 148-1 |  | 46.33593 | -119.272243 | Battelle | Richland, WA | TCA |  |  | 322.4 |  |
| 150-1 | NTIWA28573 | 47.41139 | -122.25359 | Exotic Metals Forming Co. | Kent, WA | TCE |  |  |  | 4143.4 |
| 151-1 | NTIWA18093 | 47.364259 | -122.228866 | HTB, Inc. | Kent, WA | PCE |  | 1361.0 |  |  |
| 152-1 |  | 47.686348 | -117.203511 | Johnson Matthey | Spokane, WA | MC | 45.0 |  |  |  |
| 153-1 |  | 47.517041 | -120.473557 | LE Wilson, Inc | Cashmere, WA | PCE |  | 1995.8 |  |  |
| 154-1 |  | 47.66525 | -122.3724 | MANCO Mfg | Seattle, WA | TCE |  |  |  | 1646.5 |
| 164-1 | NTI12240 | 41.539 | -90.458 | Alcoa | Riverdale, IA | PCE |  | 50849.3 |  |  |
| 165-1 | NTIVAT$2612 | 38.192 | -78.988 | American Safety Razor Inc. (VA) | Verona, VA | TCE |  |  |  | 50803.3 |
| 165-2 | NTITNT$5022 | 35.96 | -83.827 | American Safety Razor Inc. (TN) | Knoxville, TN | TCE |  |  |  | 23542.1 |
| 166-1 | NTI7218 | 40.8 | -76.44 | Arcos Alloys | Mt. Carmel, PA | PCE |  | 3684.0 |  |  |
| 167-1 | NTI2733 | 50.64192 | -71.185 | Johnson and Johnston (a.k.a. Gould Electronics) | Hampstead, NH | TCE |  |  |  | 15528.1 |
| 169-1 | NTI6360 | 41.535 | -73.03 | Olin Corp. (Somers Thin Strip, Olin Brass) | Waterbury, CT | MC | 52520.3 |  |  |  |
| 170-1 |  | 40.92 | -73.86 | Stewart Stamping Corp. (Stewart EFI) | Yonkers , NY | MC | 3311.0 |  |  |  |
| NTI59 |  | 40.5175018 | -79.8114014 | HASKELL SENATOR INTERNATIONAL | VERONA, PA | MC | 163.3 |  |  |  |
| NTI180 |  | 38.7126999 | -77.2369003 | DC DEPT CORR/LORTON REFORMATORY | Lorton, VA | MC | 23750.1 |  |  |  |
| NTI814 |  | 33.6347008 | -92.6917038 | ATLANTIC RESEARCH |  | TCA |  |  | 59.0 |  |
| NTI922 |  | 35.8064003 | -90.2421036 | HALSTEAD INDUSTRIES INCORPORATED |  | TCE |  |  |  | 99790.3 |
| NTI946 |  | 39.6469994 | -104.998802 | COLORADO MOLDED PRODUCTS CO | ENGLEWOOD, CO | TCE |  |  |  | 3991.6 |
| NTI965 |  | 40.0617981 | -105.205902 | COMPLEX TOOLING & MOLDING INC | BOULDER, CO | MC | 225.4 |  |  |  |
| NTI968 |  | 40.1433983 | -105.111504 | NYPRO COLORADO INC | LONGMONT, CO | MC | 97.6 |  |  |  |
| NTI1077 |  | 33.6651993 | -93.5932007 | CHAMPION PARTS,INC |  | TCA |  |  | 137529.2 |  |
| NTI1162 |  | 37.3195992 | -80.7270966 | Rene Composite Materials | Pearisburg, VA | MC | 2540.1 |  |  |  |
| NTI1608 |  | 39.7523994 | -104.876297 | STANLEY AVIATION CORP | AURORA, CO | TCE |  |  |  | 1333.6 |
| NTI1830 |  | 38.8087006 | -104.7248 | BOYD LIGHTING CO | COLORADO SPRINGS, CO | PCE |  | 1509.1 |  |  |
| NTI2162 |  | 38.2770996 | -104.4879 | MCDONNELL DOUGLAS ASTRONAUTICS CO | PUEBLO, CO | TCA |  |  | 454.0 |  |
| NTI3606 |  | 40.4241982 | -104.698196 | YE OLDE STRIPPE SHOPPE | GREELEY, CO | MC | 548.8 |  |  |  |
| NTI3618 |  | 39.8037987 | -104.931099 | STEWART & STEVENSON POWER INC | COMMERCE CITY, CO | TCA |  |  | 10.4 |  |
| NTI4694 |  | 40.0206985 | -105.217903 | DISPLAYTECH INC | LONGMONT, CO | MC | 92.7 |  |  |  |
| NTI5372 |  | 40.6917 | -78.2287979 | CHICAGO RIVET & MACH/TYRONE PLT | TYRONE, PA | TCE |  |  |  | 33112.2 |
| NTI5384 |  | 41.6234016 | -80.1656036 | CHANNELLOCK INC/KUSSEWAGO | MEADVILLE, PA | MC | 31601.6 |  |  |  |
| NTI5410 |  | 40.1064987 | -75.3432999 | TUBE METHODS INC/BRIDGEPORT | BRIDGEPORT, PA | TCE |  |  |  | 9434.7 |
| NTI6225 |  | 41.6246796 | -71.4919968 | STANLEY-BOSTITCH, INC. (EG) | E. GREENWICH, RI | MC | 7692.9 |  |  |  |
| NTI6320 |  | 41.853611 | -72.6997223 | JACOBS VEHICLE SYS. INC. | BLOOMFIELD, CT | MC | 9446.1 |  |  |  |
| NTI6332 |  | 41.7338905 | -72.7238922 | HAR-CONN CHROME CO. - METAL FINISHING SPECIALISTS | WEST HARTFORD, CT | PCE |  | 12314.1 |  |  |
| NTI6506 |  | 32.4614792 | -94.7333374 | LE TOURNEAUINC | LONGVIEW, TX | TCA |  |  | 154.2 |  |
| NTI6596 |  | 32.2906189 | -95.2542572 | THE TRANE COMPANY | TYLER, TX | TCE |  |  |  | 13596.7 |
| NTI7024 |  | 41.4208984 | -78.5691986 | KEYSTONE POWDERED ME/FKA KEYSTONE CARBON CO | ST MARYS, PA | TCE |  |  |  | 17055.1 |
| NTI7025 |  | 41.5551987 | -78.5833969 | KEYSTONE THERMOMETRI/WINDFALL RD | ST MARYS, PA | TCE |  |  |  | 16873.6 |
| NTI7026 |  | 41.3830986 | -78.7667007 | POWDERED METAL PRODU/ST MARYS | ST MARYS, PA | TCE |  |  |  | 3538.0 |
| NTI7049 |  | 28.98209 | -95.3433838 | THE DOW CHEMICAL CO | FREEPORT, TX | PCE,TCA |  | 4.4 | 4.4 |  |
| NTI7077 |  | 32.8268013 | -97.3837128 | EFW INC | FORT WORTH, TX | TCA |  |  | 1119.5 |  |
| NTI7150 |  | 29.6941204 | -96.7900238 | UTEX INDUSTRIES INC | WEIMER, TX | TCE |  |  |  | 619.4 |
| NTI7172 |  | 39.9011993 | -76.6287994 | GICHNER SHELTER SYS/DALLASTOWN PLT | DALLASTOWN, PA | TCE |  |  |  | 13789.2 |
| NTI7194 |  | 40.1088982 | -76.4774017 | MT JOY WIRE CORP/MT JOY | MT JOY, PA | TCE |  |  |  | 272.2 |
| NTI7203 |  | 41.2434006 | -77.0391998 | TEXTRON LYCOMING/OLIVER STREET PLT | WILLIAMSPORT, PA | PCE |  | 362.9 |  |  |
| NTI7288 |  | 40.3725014 | -75.2985992 | DELBAR PROD INC/PERKASIE | PERKASIE, PA | TCE |  |  |  | 7983.2 |
| NTI7323 |  | 40.1015015 | -75.1389008 | SPS TECH INC/ABINGTON | JENKINTOWN, PA | TCE |  |  |  | 6622.4 |
| NTI7345 |  | 40.1668015 | -75.3376999 | HANDY & HARMAN TUBE /EAST NORRITON | NORRISTOWN, PA | TCE |  |  |  | 41730.5 |
| NTI7347 |  | 40.2330017 | -75.552803 | UNIFORM TUBES INC/COLLEGEVILLE | COLLEGEVILLE, PA | MC,TCE | 181.4 |  |  | 41458.3 |
| NTI7348 |  | 40.1864014 | -75.4365005 | SUPERIOR TUBE CO/LOWER PROVIDENCE | COLLEGEVILLE, PA | TCE |  |  |  | 44361.3 |
| NTI7350 |  | 40.2575989 | -75.3292007 | PENN FISHING TACKLE /TOWAMENCIN | KULPSVILLE, PA | MC | 9434.7 |  |  |  |
| NTI7365 |  | 40.3209 | -76.0257034 | WILLIAMS METAL FINIS/SINKING SPRING | SINKING SPRING, PA | TCE |  |  |  | 7909.3 |
| NTI7367 |  | 40.3228989 | -75.9410019 | BALDWIN HDWR CORP/READING PLT | READING, PA | TCE |  |  |  | 75477.8 |
| NTI7368 |  | 40.3586006 | -75.9374008 | CARPENTER TECH CORP/READING PLT | READING, PA | PCE,TCE |  | 453.6 |  | 3719.5 |
| NTI7418 |  | 32.3767586 | -95.2776489 | BONAR PACKAGING INC | TYLER, TX | MC,PCE | 1.1 | 1.8 |  |  |
| NTI7573 |  | 32.8932991 | -96.7028809 | MARLOW INDUSTRIES INC | DALLAS, TX | TCE |  |  |  | 1289.2 |
| NTI7752 |  | 31.6643906 | -94.6628265 | JM CLIPPER CORP | NACOGDOCHES, TX | PCE |  | 91.1 |  |  |
| NTI7803 |  | 33.1375389 | -97.0453568 | BOEING CORINTH CO | CORINTH, TX | MC,TCA | 12.8 |  | 1943.4 |  |
| NTI7925 |  | 32.9057503 | -80.0997391 | BOSCH, ROBERT:CORPORATE OFFICE | CHARLESTON, SC | TCE |  |  |  | 3429.2 |
| NTI7956 |  | 34.960434 | -82.4418182 | ERNST WINTER & SONS | TRAVELERS REST, SC | PCE |  | 8821.5 |  |  |
| NTI8259 |  | 29.7267704 | -95.0772095 | OXY-VINYLSLP | LA PORTE, TX | TCA |  |  | 0.7 |  |
| NTI8273 |  | 30.2248993 | -81.6703033 | UNITED STATES NAVY | JACKSONVILLE, FL | MC | 7456.2 |  |  |  |
| NTI8297 |  | 28.3111 | -80.7092972 | HYDRO ALUMINUM | ROCKLEDGE, FL | TCE |  |  |  | 21591.0 |
| NTI8346 |  | 29.3252296 | -81.1154404 | HUDSON TOOL & DIE CO | ORMOND BEACH, FL | TCE |  |  |  | 38827.5 |
| NTI8448 |  | 34.1567726 | -86.8306503 | Cullman Products | Cullman, AL | TCE |  |  |  | 6060.0 |
| NTI8534 |  | 34.6519012 | -86.6639023 | George C. Marshall Space Flight Center | Redstone Arsenal, AL | PCE |  | 12482.9 |  |  |
| NTI8573 |  | 33.6241989 | -85.7473984 | York Group Wallace Metal Products Inc | Anniston, AL | TCE |  |  |  | 11122.1 |
| NTI8604 |  | 30.5492992 | -88.1372986 | Taylor Wharton | Theodore, AL | TCE |  |  |  | 5080.2 |
| NTI8637 |  | 29.3771305 | -98.5672607 | US AIRFORCE | SAN ANTONIO, TX | MC,PCE | 9.1 | 5841.1 |  |  |
| NTI10887 |  | 32.78479 | -97.0495224 | ZEXEL USA CORPORATION | GRAND PRAIRIE, TX | TCE |  |  |  | 11560.7 |
| NTI10900 |  | 35.1663895 | -86.565834 | LTV-COPPERWELD FAYETTEVILLE DIV. | FAYETTEVILLE, TN | PCE |  | 82100.2 |  |  |
| NTI11106 |  | 33.8242989 | -89.7984009 | HEATCRAFT INC COMMERCIAL PRODUCTS PLANT | GRENADA, MS | TCE |  |  |  | 85556.6 |
| NTI11217 |  | 28.9569397 | -95.3876495 | THE DOW CHEMICAL CO | FREEPORT, TX | PCE,TCA |  | 7.2 | 7.2 |  |
| NTI11248 |  | 38.2098007 | -85.2263031 | ROLL FORMING CORP | SHELBYVILLE, KY | TCE |  |  |  | 6350.3 |
| NTI11259 |  | 37.7773018 | -84.8528976 | MODINE CLIMATE SYSTEMS | HARRODSBURG, KY | TCE |  |  |  | 30190.8 |
| NTI11295 |  | 28.98806 | -95.3843079 | THE DOW CHEMICAL CO | CLUTE, TX | PCE,TCA |  | 25.2 | 1672.0 |  |
| NTI11307 |  | 39.0306015 | -84.444603 | FISCHER SPECIAL MFG CO | COLD SPRING, KY | TCE |  |  |  | 9582.2 |
| NTI11344 |  | 36.7360992 | -86.5621033 | DANA CORPORATION | FRANKLIN, KY | TCE |  |  |  | 21772.4 |
| NTI11368 |  | 37.6945 | -87.8743973 | RAYLOC | Morganfield, KY | TCE |  |  |  | 35380.2 |
| NTI11591 |  | 32.9132881 | -96.753418 | RAYTHEON TISYSTEMS INC | RICHARDSON, TX | TCA |  |  | 83.1 |  |
| NTI11648 |  | 39.8914986 | -83.7249985 | TRUTEC INDUSTRIES, INC. | SPRINGFIELD, OH | TCE |  |  |  | 56916.8 |
| NTI11698 |  | 40.0227814 | -86.0016708 | FIRESTONE INDUS PROD |  | PCE |  | 3374.7 |  |  |
| NTI11809 |  | 32.8334007 | -97.318161 | BEHR CLIMATE SYSTEMS INC | FORT WORTH, TX | MC | 25273.3 |  |  |  |
| NTI11837 |  | 42.4528694 | -83.0916138 | VER MAR PRODUCTS CORP | HAZEL PARK, MI | TCE |  |  |  | 4531.4 |
| NTI11865 |  | 42.3184586 | -83.8880386 | DAPCO INDUSTRIES | DEXTER, MI | MC | 7076.0 |  |  |  |
| NTI11916 |  | 42.9874001 | -84.2157364 | MOTOR PRODUCTS - OWOSSO CORPORATION | OWOSSO, MI | TCE |  |  |  | 1850.7 |
| NTI11917 |  | 42.9957809 | -84.5833817 | DANA CORPORATION, PERFECT CIRCLE DIVISION | SAINT JOHNS, MI | TCE |  |  |  | 15981.7 |
| NTI11984 |  | 43.2079811 | -86.2491226 | DANA CORPORATION - SANFORD STREET FACILITY | MUSKEGON, MI | TCE |  |  |  | 12888.3 |
| NTI11985 |  | 43.2257385 | -86.2119598 | SEALED POWER DIVISION HARVEY STREET FACI | MUSKEGON, MI | TCE |  |  |  | 9126.3 |
| NTI11994 |  | 42.9460411 | -85.6833267 | KEELER BRASS COMPANY | GRAND RAPIDS, MI | MC,TCE | 7076.0 |  |  | 34600.4 |
| NTI12011 |  | 44.2530289 | -85.4217682 | CADILLAC RUBBER & PLASTICS INC | CADILLAC, MI | TCE |  |  |  | 5660.8 |
| NTI12015 |  | 29.7356892 | -95.0910797 | DSI TRANSPORTS INC | HOUSTON, TX | MC,PCE,TCA,TCE | 0.4 | 18.2 | 0.2 | 0.2 |
| NTI12294 |  | 29.9774399 | -95.2758636 | HYDRIL ELASTOMER & INDUSTRIAL PROD | HUMBLE, TX | PCE |  | 9699.4 |  |  |
| NTI12320 |  | 44.8801003 | -93.2052994 | Northwest Airlines Inc/Mpls/St Paul Airp | ST. PAUL, MN | TCE |  |  |  | 21648.9 |
| NTI12333 |  | 44.8608017 | -93.5250015 | Roberts Automatic Products | CHANHASSEN, MN | MC | 5328.8 |  |  |  |
| NTI12350 |  | 44.9826012 | -93.2182007 | Globe Tool & Manufacturing Co Inc | MINNEAPOLIS, MN | TCE |  |  |  | 9307.7 |
| NTI12355 |  | 45 | -93.3602982 | Honeywell - Golden Valley - Home & Bldg | GOLDEN VALLEY, MN | TCE |  |  |  | 10315.1 |
| NTI12371 |  | 32.8820114 | -97.0481262 | DALLAS FORTWORTH INTRNTNL AIRPORT | GRAPEVINE, TX | PCE,TCA |  | 1.1 | 1.1 |  |
| NTI12393 |  | 43.6613007 | -94.5037994 | Weigh-Tronix Inc | FAIRMONT, MN | TCE |  |  |  | 1417.4 |
| NTI12595 |  | 32.7748184 | -97.0593109 | BELL HELICOPTER TEXTRON INC | GRAND PRAIRIE, TX | MC,PCE | 377.6 | 34260.1 |  |  |
| NTI12689 |  | 38.5433006 | -90.3289032 | WHITE RODGERS DIVISION |  | TCE |  |  |  | 10732.4 |
| NTI12749 |  | 37.1702423 | -97.0278702 | GREIF BROS. CORPORATION | WINFIELD, KS | TCE |  |  |  | 6190.6 |
| NTI12925 |  | 35.5199013 | -97.6417999 | Gulfstream Aerospace Technologies |  | TCE |  |  |  | 15606.3 |
| NTI12974 |  | 36.3736992 | -95.8298035 | Allied Signal - Lori, Inc. | Tulsa, OK | PCE |  | 5561.0 |  |  |
| NTI12985 |  | 34.8852997 | -95.9488983 | McAlester Army Ammunition Plant |  | PCE,TCA |  | 36.3 | 102.1 |  |
| NTI13146 |  | 39.6506004 | -105.028 | OAKLEY INDUSTRIES INC OAKLEY TUBE DIV | ENGLEWOOD, CO | TCE |  |  |  | 907.2 |
| NTI13238 |  | 29.7040195 | -95.3980484 | THERMAL ENERGY COOPERATIVE | HOUSTON, TX | PCE |  | 0.1 |  |  |
| NTI13294 |  | 33.868 | -118.312401 | ALLIEDSIGNAL AEROSPACE SYSTEMS |  | TCA |  |  | 6241.7 |  |
| NTI13336 |  | 45.5438004 | -122.466904 | Boeing Company (The) | PORTLAND, OR | PCE,TCA |  | 5098.4 | 9.1 |  |
| NTI18314 |  | 39.3202019 | -76.4974976 | U.S. CAN - STEELTIN DIVISION | ROSEDALE, MD | TCE |  |  |  | 825.5 |
| NTI18329 |  | 33.6375999 | -85.9197006 | ANNISTON ARMY DEPOT | Anniston, AL | MC,TCE | 48507.2 |  |  | 9471.0 |
| NTI18485 |  | 33.7416687 | -112.008331 | GARRETT ENGINE DIVISION |  | PCE,TCA |  | 9248.7 | 195.1 |  |
| NTI18497 |  | 33.3735619 | -111.820717 | HEXCEL SATELLITE PRODUCTS | GILBERT, AZ | MC | 39.9 |  |  |  |
| NTI18503 |  | 33.5194397 | -112.616669 | INERTIA DYNAMICS CORP |  | PCE |  | 1059.1 |  |  |
| NTI18505 |  | 33.5027809 | -112.51944 | INTEL T AND A |  | PCE |  | 701.8 |  |  |
| NTI18526 |  | 33.7027817 | -112.622223 | MEDTRONIC MICRO REL |  | MC,PCE | 0.0 | 810.3 |  |  |
| NTI18533 |  | 33.4819603 | -111.891907 | MICROSEMI CORP | SCOTTSDALE, AZ | MC | 159.7 |  |  |  |
| NTI18535 |  | 33.7777786 | -112.508331 | MOTOROLA GEG COMMUNICATION DIV |  | PCE |  | 897.9 |  |  |
| NTI18551 |  | 33.4407997 | -112.109901 | PAN-GLO WEST |  | PCE |  | 3.9 |  |  |
| NTI18598 |  | 33.4607697 | -112.104897 | TREFFERS PRECISION INC | PHOENIX, AZ | PCE |  | 635.0 |  |  |
| NTI18603 |  | 33.5722198 | -112.625 | U-HAUL ASSEMBLY PLANT |  | PCE |  | 467.9 |  |  |
| NTI18609 |  | 33.7027817 | -112.166672 | UNITED METRO MATERIALS PLT #1 (TANNER) |  | PCE |  | 455.7 |  |  |
| NTI18760 |  | 37.7402 | -122.216904 | BAXTER HEALTHCARE CORPORATION, | OAKLAND, CA | MC | 15.0 |  |  |  |
| NTI18906 |  | 37.6795998 | -121.764 | DOE-KAO SANDIA NATIONAL LABORA | LIVERMORE, CA | MC,PCE,TCA,TCE | 6.6 | 3.7 | 114.8 | 91.3 |
| NTI18907 |  | 37.7092018 | -121.933701 | DOLD'S WORKSHOP | DUBLIN, CA | MC | 3008.0 |  |  |  |
| NTI18914 |  | 37.6534996 | -121.9571 | DUBLIN SAN RAMON SERVICES DIST | PLEASANTON, CA | TCA |  |  | 49.5 |  |
| NTI19032 |  | 37.6436691 | -122.134079 | HTB INC | HAYWARD, CA | TCA,TCE |  |  | 6662.4 | 3649.8 |
| NTI19036 |  | 37.4894638 | -121.93351 | IHT CORPORATION | FREMONT, CA | TCA,TCE |  |  | 308.5 | 0.9 |
| NTI19042 |  | 37.8552017 | -122.295303 | INLITE CORPORATION | BERKELEY, CA | TCA |  |  | 1086.0 |  |
| NTI19053 |  | 37.7737999 | -122.250603 | J D HARPE FURNITURE FINISHERS | ALAMEDA, CA | MC | 882.3 |  |  |  |
| NTI19067 |  | 37.6430016 | -121.889297 | KAISER ALUMINUM & CHEMICAL COR | PLEASANTON, CA | TCA |  |  | 24.3 |  |
| NTI19090 |  | 37.8812065 | -122.23703 | LAWRENCE BERKELEY NATIONAL LAB | BERKELEY, CA | TCA,TCE |  |  | 65.0 | 1.7 |
| NTI19091 |  | 37.6928329 | -121.717239 | LAWRENCE LIVERMORE NATIONAL LA | LIVERMORE, CA | TCA,TCE |  |  | 99.0 | 0.3 |
| NTI19512 |  | 39.1977997 | -122.027298 | PIRELLI CABLE CORPORATION | COLUSA, CA | TCA |  |  | 3937.6 |  |
| NTI19632 |  | 38.0256004 | -121.940498 | DEXTER HYSOL AEROSPACE, INC | PITTSBURG, CA | TCA |  |  | 89.9 |  |
| NTI19793 |  | 37.924099 | -122.3629 | PILGRIM FIREPLACE EQUIPMENT CO | RICHMOND, CA | TCA |  |  | 147.2 |  |
| NTI19859 |  | 37.9636002 | -122.066597 | SYSTRON DONNER INERTIAL DIVISI | CONCORD, CA | TCA |  |  | 13.4 |  |
| NTI19913 |  | 36.7514 | -119.733101 | AMOCO FOAM PRODUCTS COMPANY | FRESNO, CA | TCA |  |  | 867.3 |  |
| NTI19921 |  | 36.7118988 | -119.765297 | CHAMPION PARTS WESTERN DIVISIO | FRESNO, CA | TCA |  |  | 34936.6 |  |
| NTI19927 |  | 36.5084 | -119.557098 | DEL MONTE FOODS PLANT NO. 25 | KINGSBURG, CA | MC | 77.5 |  |  |  |
| NTI20225 |  | 33.919899 | -118.276398 | AAA ADVANCE FINISHING, INC | LOS ANGELES, CA | TCA |  |  | 1639.3 |  |
| NTI20228 |  | 34.0298996 | -118.375504 | ABBOTT TRANSISTOR LABORATORIES | LOS ANGELES, CA | TCA |  |  | 3425.0 |  |
| NTI20230 |  | 33.8072014 | -118.166702 | ACCURATE METAL FABRICATORS INC | SIGNAL HILL, CA | TCA |  |  | 1107.7 |  |
| NTI20231 |  | 33.8997993 | -118.167999 | ACE CLEARWATER ENTER. | PARAMOUNT, CA | TCA |  |  | 2245.3 |  |
| NTI20232 |  | 33.8678017 | -118.243202 | ACE CLEARWATER ENTERPRISES | COMPTON, CA | TCA |  |  | 1197.5 |  |
| NTI20234 |  | 34.0199013 | -117.963799 | ACORN ENGINEERING CO | INDUSTRY, CA | TCA |  |  | 17770.9 |  |
| NTI20237 |  | 34.1327019 | -118.268799 | ADAMS RITE SABRE INTERNATIONAL | GLENDALE, CA | PCE |  | 1010.6 |  |  |
| NTI20241 |  | 33.8998985 | -118.308502 | ADVANCED COATING & SILKSCREENI | GARDENA, CA | TCA |  |  | 2522.4 |  |
| NTI20242 |  | 34.2150002 | -118.487099 | AELCO CORP | VAN NUYS, CA | TCA |  |  | 4276.0 |  |
| NTI20243 |  | 34.0998993 | -118.246597 | AERO ENGINES INC | LOS ANGELES, CA | MC,TCA,TCE | 1331.3 |  | 6678.2 | 139.7 |
| NTI20245 |  | 34.1198997 | -117.9216 | AEROJET GENCORP, AEROJET ELECT | AZUSA, CA | TCA |  |  | 1465.1 |  |
| NTI20247 |  | 33.889801 | -118.178596 | AEROSPACE ALUMINUM HEAT TREATI | PARAMOUNT, CA | TCA |  |  | 12886.5 |  |
| NTI20249 |  | 33.8819008 | -118.275803 | AHF DUCOMMUN INC | CARSON, CA | TCA |  |  | 277.1 |  |
| NTI20252 |  | 33.9595985 | -118.071404 | AIR LIQUIDE AMERICAN CORP | SANTA FE SPRINGS, CA | TCA |  |  | 796.1 |  |
| NTI20253 |  | 34.1500015 | -118.073799 | AIR LOGISTICS CORP | PASADENA, CA | TCA |  |  | 872.7 |  |
| NTI20256 |  | 34.2298012 | -118.367897 | AIRCRAFT CYLINDER & TURBINE IN | SUN VALLEY, CA | PCE |  | 2447.9 |  |  |
| NTI20257 |  | 33.9898987 | -118.223297 | AIRCRAFT X-RAY LABS INC | HUNTINGTON PARK, CA | TCA |  |  | 3805.6 |  |
| NTI20268 |  | 34.2999001 | -118.477699 | ALLIED-SIGNAL OCEAN SYSTEMS | SYLMAR, CA | TCA |  |  | 18845.4 |  |
| NTI20272 |  | 33.8799019 | -118.016296 | AMADA MFG AMERICA, INC | LA MIRADA, CA | PCE |  | 7630.3 |  |  |
| NTI20273 |  | 33.9398994 | -118.417397 | AMERICAN AIRLINES INC (EIS USE | LOS ANGELES, CA | MC,TCA | 2689.2 |  | 9264.7 |  |
| NTI20276 |  | 34.2699013 | -118.433701 | AMERICAN ETCHING & MFG CO | PACOIMA, CA | PCE,TCA |  | 1105.9 | 151.5 |  |
| NTI20284 |  | 33.8451004 | -118.340103 | AMP INCORPORATED | TORRANCE, CA | TCA |  |  | 2554.5 |  |
| NTI20286 |  | 33.9299011 | -118.168404 | ANADITE INC | SOUTH GATE, CA | PCE,TCA |  | 7326.4 | 3087.1 |  |
| NTI20294 |  | 33.9898987 | -118.223297 | ANGELUS SANITARY CAN MACHINE C | VERNON, CA | TCA |  |  | 703.7 |  |
| NTI20298 |  | 34.2899017 | -118.4123 | ANTHONY MANUFACTURING CO INC | SAN FERNANDO, CA | TCA |  |  | 22470.8 |  |
| NTI20304 |  | 33.7699013 | -118.2202 | ARCO CQC KILN | WILMINGTON, CA | TCA |  |  | 555.8 |  |
| NTI20307 |  | 33.7999001 | -118.2314 | ARCO PRODUCTS CO | CARSON, CA | TCA |  |  | 25315.6 |  |
| NTI20317 |  | 34.0699005 | -118.170303 | ARROWHEAD BRASS PROD. INC | LOS ANGELES, CA | PCE |  | 5767.9 |  |  |
| NTI20327 |  | 33.8953018 | -118.286903 | ASSOC SPRING BARNES GRP INC,AS | GARDENA, CA | TCA |  |  | 528.0 |  |
| NTI20328 |  | 33.9197998 | -118.1791 | ASTRO ALUMINUM TREATING CO INC | SOUTH GATE, CA | TCA |  |  | 38197.9 |  |
| NTI20335 |  | 34.1441002 | -118.008598 | AVERY DENNISON | MONROVIA, CA | TCA |  |  | 13018.1 |  |
| NTI20336 |  | 34.1717987 | -118.323601 | AVIBANK MFG INC | BURBANK, CA | PCE,TCA |  | 4.0 | 5265.5 |  |
| NTI20337 |  | 34.2262001 | -118.3787 | AVX FILTERS CORP | SUN VALLEY, CA | MC,TCA | 759.8 |  | 1313.1 |  |
| NTI20348 |  | 34.2083015 | -118.443497 | BW/IP INTERNATIONAL INC | VAN NUYS, CA | TCA |  |  | 832.1 |  |
| NTI20353 |  | 34.0298004 | -118.440498 | BARLOW SPECIALTY ADVERTISING I | LOS ANGELES, CA | MC,TCA | 119.7 |  | 1755.3 |  |
| NTI20357 |  | 34.0868988 | -118.0513 | BEAGLE MFG CO INC | EL MONTE, CA | MC | 128.8 |  |  |  |
| NTI20365 |  | 34.0199013 | -117.974701 | BENTLEY MILLS INC | INDUSTRY, CA | TCA |  |  | 270.3 |  |
| NTI20370 |  | 33.8599014 | -118.1026 | BLAIR'S METAL POLISHING | CERRITOS, CA | TCA |  |  | 15739.2 |  |
| NTI20372 |  | 34.1898003 | -118.389 | BOBRICK WASHROOM EQUIP INC | NORTH HOLLYWOOD, CA | TCA |  |  | 478.3 |  |
| NTI20389 |  | 34.092701 | -117.888802 | BROWN INTL CORP | COVINA, CA | TCA |  |  | 263.1 |  |
| NTI20390 |  | 33.9334984 | -118.071098 | BRUNO'S ELECTRIC MOTOR REPAIR | SANTA FE SPRINGS, CA | PCE |  | 249.5 |  |  |
| NTI20396 |  | 34.169899 | -118.301903 | BURBANK STEEL TREATING INC | BURBANK, CA | TCA |  |  | 4803.5 |  |
| NTI20398 |  | 34.2868004 | -118.433998 | BURR MASTER INC | SAN FERNANDO, CA | TCA |  |  | 334.4 |  |
| NTI20411 |  | 34.0598984 | -118.170197 | CAL ST UNIV LA | LOS ANGELES, CA | TCE |  |  |  | 108.9 |
| NTI20415 |  | 34.0399017 | -117.790802 | CAL ST, POLYTECHNIC UNIV, POMO | POMONA, CA | TCE |  |  |  | 128.8 |
| NTI20420 |  | 33.9659996 | -118.0606 | CAL-TRON PLATING INC | SANTA FE SPRINGS, CA | TCA |  |  | 13607.8 |  |
| NTI20456 |  | 33.9598007 | -118.374397 | CHARLES CAINE CO INC | LOS ANGELES, CA | TCA |  |  | 2239.2 |  |
| NTI20467 |  | 33.9098015 | -118.416901 | CHEVRON PRODUCTS CO. | EL SEGUNDO, CA | TCA |  |  | 45.0 |  |
| NTI20484 |  | 33.8681984 | -118.199997 | COAST METAL CRAFT CORP | RANCHO DOMINGUEZ, CA | TCA |  |  | 4385.8 |  |
| NTI20491 |  | 34.2699013 | -118.433701 | COLOR-TEC INDUSTRIAL FINISHING | PACOIMA, CA | TCA |  |  | 2068.4 |  |
| NTI20497 |  | 34.1399002 | -117.9869 | COMPOSITE STRUCTURES | MONROVIA, CA | TCA |  |  | 44640.3 |  |
| NTI20502 |  | 33.9104996 | -118.384399 | CONSOL CONTROLS CORP PLT NO. 4 | EL SEGUNDO, CA | TCA |  |  | 761.1 |  |
| NTI20503 |  | 34.2098999 | -118.454399 | CONSOL FABRICATORS CORP | SUN VALLEY, CA | TCA |  |  | 614.6 |  |
| NTI20508 |  | 34.0798988 | -118.333 | CONSOLIDATED FILM INDUSTRIES | HOLLYWOOD, CA | PCE,TCA |  | 5297.9 | 90032.6 |  |
| NTI20511 |  | 33.9398003 | -118.4282 | CONTINENTAL AIRLINES INC (NSR | LOS ANGELES, CA | MC,TCA | 12854.0 |  | 3649.0 |  |
| NTI20517 |  | 33.8797989 | -118.264999 | CORONET MFG CO INC | GARDENA, CA | PCE |  | 3653.2 |  |  |
| NTI20521 |  | 33.8398018 | -118.340103 | COSMODYNE CORP | TORRANCE, CA | TCA |  |  | 2109.2 |  |
| NTI20522 |  | 34.1506004 | -118.2799 | COURTAULDS AEROSPACE INC | GLENDALE, CA | TCA |  |  | 71722.9 |  |
| NTI20527 |  | 34.1898003 | -118.345596 | CRANE CO, HYDRO-AIRE DIV | BURBANK, CA | MC,TCA | 1730.5 |  | 11801.1 |  |
| NTI20528 |  | 34.0471992 | -118.0616 | CRANEVEYOR CORP | SOUTH EL MONTE, CA | TCA |  |  | 2993.7 |  |
| NTI20533 |  | 34.0798988 | -118.051201 | CROWN CITY PLATING CO | EL MONTE, CA | MC,TCA | 655.4 |  | 6621.1 |  |
| NTI20538 |  | 34.2425003 | -118.5961 | CUSTOM CONTROL SENSORS INC | CHATSWORTH, CA | PCE,TCA |  | 330.7 | 1621.1 |  |
| NTI20543 |  | 33.8270988 | -118.339897 | CV INTL INC | TORRANCE, CA | TCA |  |  | 573.8 |  |
| NTI20551 |  | 33.8535004 | -118.232201 | DAICO IND INC | COMPTON, CA | TCA |  |  | 1068.4 |  |
| NTI20553 |  | 33.9968987 | -117.920303 | DARNELL CORP | INDUSTRY, CA | MC,TCA | 217.3 |  | 309.5 |  |
| NTI20555 |  | 34.0998993 | -118.008102 | DATABYTE TECHNOLOGY INC | ARCADIA, CA | TCA |  |  | 382.1 |  |
| NTI20559 |  | 34.1515999 | -118.084602 | DATATAPE INC | PASADENA, CA | TCA |  |  | 2281.6 |  |
| NTI20571 |  | 33.9149017 | -118.3088 | DEL MAR DIE CASTING CO., INC | GARDENA, CA | TCE |  |  |  | 553.4 |
| NTI20572 |  | 33.9384003 | -118.384903 | DELTA AIR LINES, INC | LOS ANGELES, CA | TCA |  |  | 326.0 |  |
| NTI20575 |  | 34.0900002 | -118.300598 | DELUXE LABORATORIES INC,DELUXE | HOLLYWOOD, CA | TCA |  |  | 196655.4 |  |
| NTI20579 |  | 33.8997993 | -118.286903 | DEUTSCH CO, METAL COMPONENTS D | GARDENA, CA | TCA |  |  | 16335.8 |  |
| NTI20583 |  | 34.0243988 | -117.974701 | DEXTER CORP, ELECTRONIC MATERI | INDUSTRY, CA | TCA |  |  | 349.3 |  |
| NTI20588 |  | 33.8997993 | -118.286903 | DIE CAST PROD. INC | GARDENA, CA | PCE |  | 1091.3 |  |  |
| NTI20593 |  | 34.2336998 | -118.574303 | DOOLING BROS INC | CHATSWORTH, CA | TCA |  |  | 637.8 |  |
| NTI20594 |  | 34.0004005 | -118.147697 | DORFILE COMPANY | COMMERCE, CA | TCA |  |  | 9836.1 |  |
| NTI20600 |  | 33.8958015 | -118.049004 | DRAGON VALVE CO INC | NORWALK, CA | MC,TCA,TCE | 612.8 |  | 1021.5 | 50.3 |
| NTI20605 |  | 33.839901 | -118.329201 | DOW CHEM U.S.A. (NSR USE) | TORRANCE, CA | MC | 816.5 |  |  |  |
| NTI20606 |  | 33.8480988 | -118.232101 | E J S LIGHTING CORP | COMPTON, CA | PCE |  | 9871.1 |  |  |
| NTI20617 |  | 34.0960999 | -118.029701 | EDMONDSON ENTER. INC | TEMPLE CITY, CA | MC,PCE,TCA | 292.1 | 365.1 | 13723.4 |  |
| NTI20618 |  | 34.1399002 | -118.279701 | EEMCO, DATRON INC DIV | LOS ANGELES, CA | MC,PCE,TCA | 426.0 | 1289.8 | 1886.0 |  |
| NTI20619 |  | 34.0399017 | -118.039902 | EEMUS MFG CORP | SOUTH EL MONTE, CA | TCA |  |  | 1055.1 |  |
| NTI20620 |  | 34.089901 | -117.877899 | EG & G POWER SYSTEMS | COVINA, CA | TCA |  |  | 4483.1 |  |
| NTI20623 |  | 33.9173012 | -118.059998 | ELECTRO-MAG | WHITTIER, CA | TCA |  |  | 743.3 |  |
| NTI20627 |  | 33.9099007 | -118.395203 | ELECTROPLY INC | EL SEGUNDO, CA | TCA |  |  | 11283.1 |  |
| NTI20628 |  | 33.8599014 | -118.210701 | ELLIOTT'S DESIGNS INC | RANCHO DOMINGUEZ, CA | TCA |  |  | 14719.1 |  |
| NTI20639 |  | 33.8236008 | -118.329002 | EXCELLON AUTOMATION | TORRANCE, CA | TCA |  |  | 6559.4 |  |
| NTI20644 |  | 34.1902008 | -118.5952 | FABER ENTER. INC | CANOGA PARK, CA | TCA |  |  | 5951.2 |  |
| NTI20648 |  | 33.8097992 | -118.350403 | FAIRCHILD SOUTH BAY OPERATION | TORRANCE, CA | TCA |  |  | 0.9 |  |
| NTI20663 |  | 34.0514984 | -118.267502 | FIRST INTERSTATE BANK OF CALIF | LOS ANGELES, CA | TCA |  |  | 41.6 |  |
| NTI20675 |  | 34.1198997 | -118.257698 | FOREST LAWN MEM PARK ASSOC | GLENDALE, CA | MC,TCA | 44.9 |  | 394.2 |  |
| NTI20677 |  | 34.1693001 | -118.301804 | FORTNER ENGINEERING & MFG INC | GLENDALE, CA | TCA |  |  | 525.9 |  |
| NTI20679 |  | 34.1498985 | -118.334099 | FOTO-KEM /FOTO TRONICS | BURBANK, CA | TCA |  |  | 12575.8 |  |
| NTI20681 |  | 34.2056999 | -118.356697 | FOUR MEDIA LABORATORY | BURBANK, CA | TCA |  |  | 7024.2 |  |
| NTI20685 |  | 33.8799019 | -118.048798 | FREDRICK RAMOND, INC | CERRITOS, CA | TCA |  |  | 7576.4 |  |
| NTI20687 |  | 33.8723984 | -118.318901 | FREEMAN PRODUCTS, DIV AVNET, I | TORRANCE, CA | TCA |  |  | 9505.0 |  |
| NTI20688 |  | 33.9897995 | -117.898499 | FREEMARC DESIGNS | INDUSTRY, CA | TCA |  |  | 150.2 |  |
| NTI20695 |  | 33.8092003 | -118.328796 | GAMMA-F CORP | TORRANCE, CA | TCA |  |  | 12918.3 |  |
| NTI20698 |  | 34.0928993 | -117.726196 | GARNER GLASS CO | CLAREMONT, CA | TCE |  |  |  | 709.9 |
| NTI20700 |  | 33.8675003 | -118.275597 | GASKET MFG CO INC | GARDENA, CA | TCA |  |  | 3262.7 |  |
| NTI20725 |  | 34.0098991 | -118.191101 | GRANA INDUSTRIAL FINISHERS | LOS ANGELES, CA | TCA |  |  | 3284.5 |  |
| NTI20728 |  | 34.2198982 | -118.378601 | GRAPHIC FINISHES INC | SUN VALLEY, CA | TCA |  |  | 3978.0 |  |
| NTI20749 |  | 33.8098984 | -118.145103 | HAGELIN AIRCRAFT MOTORS CO INC | LONG BEACH, CA | MC,TCA | 374.7 |  | 263.1 |  |
| NTI20752 |  | 33.8997993 | -118.2761 | HARDEN INDUSTRIES | LOS ANGELES, CA | MC,PCE | 1653.3 | 4305.5 |  |  |
| NTI20756 |  | 34.200901 | -118.378304 | HAWKER PACIFIC INC | SUN VALLEY, CA | TCA |  |  | 6162.5 |  |
| NTI20758 |  | 34.0499001 | -117.801697 | HAYWARD POOL PRODUCTS INC | POMONA, CA | MC,TCA | 13063.5 |  | 114.6 |  |
| NTI20768 |  | 34.0499001 | -118.191704 | HIGHLAND AUTO & TRUCK SUPPLY | LOS ANGELES, CA | TCA |  |  | 968.4 |  |
| NTI20770 |  | 33.8885994 | -118.048897 | HILLERICH & BRADSBY COMPANY, I | SANTA FE SPRINGS, CA | TCA |  |  | 7039.8 |  |
| NTI20777 |  | 34.0499001 | -117.996696 | HOUSE OF PACKAGING, INC | INDUSTRY, CA | TCA |  |  | 22143.4 |  |
| NTI20781 |  | 33.8199005 | -118.156097 | HUCK INTERNATIONAL - DEUTSCH O | LAKEWOOD, CA | TCA |  |  | 20458.4 |  |
| NTI20787 |  | 33.9157982 | -118.395302 | HUGHES AIRCRAFT CO, EDSG | EL SEGUNDO, CA | MC,TCA | 2.0 |  | 8845.8 |  |
| NTI20792 |  | 33.8198013 | -118.210098 | HUGHES TECHNICAL SERVICES COMP | LONG BEACH, CA | TCA |  |  | 425.0 |  |
| NTI20794 |  | 33.7658005 | -118.252502 | HUGO NEU-PROLER CO | TERMINAL ISLAND, CA | TCA |  |  | 503.5 |  |
| NTI20801 |  | 33.9989014 | -117.898598 | HYDRO TECH CHEM CORP | INDUSTRY, CA | TCA |  |  | 18332.4 |  |
| NTI20807 |  | 33.9099007 | -118.243797 | IDEAL METAL PROCESSING CO | COMPTON, CA | TCA |  |  | 9684.6 |  |
| NTI20809 |  | 33.896801 | -118.038101 | IMB ELECTRONIC PRODUCTS INC | SANTA FE SPRINGS, CA | TCA |  |  | 2526.3 |  |
| NTI20815 |  | 34.210701 | -118.465302 | INDUSTRIAL ELECTRONIC ENGINEER | VAN NUYS, CA | TCA |  |  | 1740.8 |  |
| NTI20820 |  | 33.9799995 | -118.2015 | INDUSTRIAL STEEL TREATING CO, | HUNTINGTON PARK, CA | TCA |  |  | 45012.2 |  |
| NTI20827 |  | 33.9193001 | -118.406197 | INTERNATIONAL RECTIFIER CORP | EL SEGUNDO, CA | PCE,TCA |  | 1545.4 | 45.1 |  |
| NTI20829 |  | 33.9850998 | -118.407303 | INTERNATIONL AUTO BODY | CULVER CITY, CA | TCA |  |  | 425.1 |  |
| NTI20836 |  | 34.0172005 | -117.974602 | ITT BARTON | INDUSTRY, CA | TCA |  |  | 2942.5 |  |
| NTI20840 |  | 33.9598999 | -118.147102 | J. P. TURGEON & SONS INC | BELL GARDENS, CA | TCA |  |  | 22268.2 |  |
| NTI20844 |  | 34.1992722 | -118.34362 | JANCO CORP | BURBANK, CA | TCA |  |  | 2224.9 |  |
| NTI20845 |  | 34.2198982 | -118.508904 | JBL INC | NORTHRIDGE, CA | TCA |  |  | 6167.7 |  |
| NTI20860 |  | 34.0001984 | -118.071899 | KATER-CRAFTS BOOKBINDERS | PICO RIVERA, CA | TCE |  |  |  | 314.3 |
| NTI20861 |  | 33.9098015 | -118.059898 | KEENE CORP, REINHOLD INDUSTRIE | SANTA FE SPRINGS, CA | MC,TCA | 4309.1 |  | 222.3 |  |
| NTI20865 |  | 34.030899 | -118.256401 | KEYSTONE ENGINEERING CO | LOS ANGELES, CA | TCA |  |  | 210.3 |  |
| NTI20877 |  | 33.9986992 | -118.234299 | L & F IND | HUNTINGTON PARK, CA | TCA |  |  | 272.6 |  |
| NTI20890 |  | 33.9243011 | -118.438698 | LA CITY, HYPERION TREATMENT PL | PLAYA DEL REY, CA | MC,TCA | 9.5 |  | 66.7 |  |
| NTI20895 |  | 34.1999016 | -118.443398 | LA CITY, DWP | VAN NUYS, CA | TCA |  |  | 553.8 |  |
| NTI20904 |  | 34.0382004 | -118.245697 | LA CO., METROPOLITAN TRANS AUT | LOS ANGELES, CA | MC,TCA | 32.2 |  | 432.3 |  |
| NTI20918 |  | 33.821701 | -118.339798 | LA GARD INC | TORRANCE, CA | TCA |  |  | 145.5 |  |
| NTI20919 |  | 34.2075005 | -118.356697 | LA GAUGE CO INC | SUN VALLEY, CA | TCA |  |  | 855.9 |  |
| NTI20926 |  | 33.7747002 | -118.263397 | LAIDLAW ENVIRONMENTAL SERVICES | WILMINGTON, CA | MC,PCE,TCA | 28.5 | 0.3 | 25.0 |  |
| NTI20929 |  | 34.0129013 | -117.952904 | LANSCO DIE CASTING INC/INDUSTR | INDUSTRY, CA | TCA |  |  | 10285.7 |  |
| NTI20930 |  | 34.051899 | -118.040001 | LAWSON HUGHES CO., INC | SOUTH EL MONTE, CA | TCA |  |  | 3603.4 |  |
| NTI20935 |  | 33.8799019 | -118.048798 | LEFIELL MFG CO | SANTA FE SPRINGS, CA | TCA |  |  | 94655.3 |  |
| NTI20940 |  | 34.0098991 | -117.833801 | LIBBEY GLASS INC | INDUSTRY, CA | MC | 34.3 |  |  |  |
| NTI20942 |  | 33.8768997 | -118.232498 | LIGHTOLIER INC | COMPTON, CA | MC,TCA | 2497.9 |  | 10657.2 |  |
| NTI20950 |  | 33.889801 | -118.178596 | LOCKHART IND INC | PARAMOUNT, CA | PCE |  | 5102.0 |  |  |
| NTI20951 |  | 34.5812988 | -118.133797 | LOCKHEED MARTIN SKUNK WORKS | PALMDALE, CA | PCE,TCA |  | 0.0 | 1532.9 |  |
| NTI20955 |  | 33.7798996 | -118.166298 | LONG BEACH PUBLIC TRANPORTATIO | LONG BEACH, CA | MC,TCA | 19.4 |  | 2.3 |  |
| NTI20959 |  | 34.1515999 | -118.084602 | LORAL ELECTRO-OPTICAL SYSTEMS | PASADENA, CA | TCA |  |  | 1555.8 |  |
| NTI20975 |  | 34.2298012 | -118.595901 | MACCAULEY INSTRUMENTS CORP | CHATSWORTH, CA | TCA |  |  | 2947.4 |  |
| NTI20982 |  | 33.8387985 | -118.339996 | MAGNAVOX ELECTRONIC SYSTEMS CO | TORRANCE, CA | PCE,TCA |  | 314.8 | 3996.2 |  |
| NTI20989 |  | 34.0783005 | -117.888603 | MARLEE MANUFACTURING, INC. | COVINA, CA | TCA |  |  | 764.8 |  |
| NTI20998 |  | 34.2498016 | -118.400803 | MAYONI ENTERPRISES | PACOIMA, CA | TCA |  |  | 5430.0 |  |
| NTI21002 |  | 34.1399002 | -117.9869 | MCDONNELL DOUGLAS AEROSPACE | MONROVIA, CA | TCA |  |  | 5156.0 |  |
| NTI21005 |  | 33.889801 | -118.276001 | MECH METAL FINISHING CO | GARDENA, CA | TCA |  |  | 14549.0 |  |
| NTI21008 |  | 34.2159996 | -118.476196 | MEGA SOUND INC,MAGNETIC PRODUC | VAN NUYS, CA | TCA |  |  | 232.0 |  |
| NTI21011 |  | 34.1753998 | -118.323601 | MENASCO MFG CO (EIS USE) | BURBANK, CA | TCA |  |  | 36737.8 |  |
| NTI21017 |  | 33.8153992 | -118.253197 | METAL CONTAINER CORP OF CALIFO | CARSON, CA | TCA |  |  | 9.1 |  |
| NTI21018 |  | 33.9499016 | -118.157799 | METAL SURFACES INC | BELL GARDENS, CA | PCE,TCA |  | 1602.1 | 14636.5 |  |
| NTI21019 |  | 34.134201 | -118.008499 | METRIC MACHINING | MONROVIA, CA | PCE |  | 327.0 |  |  |
| NTI21020 |  | 33.7756996 | -118.252701 | METROPOLITAN STEVEDORE CO | WILMINGTON, CA | PCE,TCA |  | 49.1 | 143.5 |  |
| NTI21030 |  | 34.1693001 | -118.301804 | MINARIK ELECTRIC CO. | GLENDALE, CA | TCA |  |  | 235.9 |  |
| NTI21044 |  | 34.0211983 | -118.234596 | MONICO ALLOYS, INC | LOS ANGELES, CA | TCA |  |  | 3556.6 |  |
| NTI21045 |  | 33.9841995 | -118.147499 | MONOGRAM AEROSPACE FASTENERS, | LOS ANGELES, CA | TCA |  |  | 233.1 |  |
| NTI21046 |  | 33.9258995 | -118.114197 | MONOGRAM IND, PEACOCK ENGINEER | NORWALK, CA | TCA |  |  | 6891.9 |  |
| NTI21050 |  | 34.0038986 | -118.1586 | MOTO-PARTS EXCHANGE CO INC | COMMERCE, CA | TCA |  |  | 3257.7 |  |
| NTI21058 |  | 33.8400002 | -118.232002 | NALCO CHEMICAL CO | CARSON, CA | MC | 10.0 |  |  |  |
| NTI21059 |  | 34.1860046 | -118.17057 | NASA JET PROPULSION LAB | PASADENA, CA | TCA |  |  | 906.3 |  |
| NTI21066 |  | 33.9398994 | -118.3741 | NATL TECH SYS | LOS ANGELES, CA | TCA |  |  | 6466.8 |  |
| NTI21068 |  | 34.0798988 | -118.040398 | NAVCOM DEFENSE ELECTRONICS INC | EL MONTE, CA | TCA |  |  | 3423.3 |  |
| NTI21070 |  | 34.1099014 | -118.246696 | NELSON NAME PLATE CO | LOS ANGELES, CA | TCA |  |  | 24615.5 |  |
| NTI21071 |  | 34.2598991 | -118.574699 | NETWORKS ELECTRONIC CORP | CHATSWORTH, CA | MC,TCA | 35.5 |  | 7584.1 |  |
| NTI21072 |  | 33.9297981 | -118.060204 | NEWMARK PROD. INC | SANTA FE SPRINGS, CA | TCA |  |  | 2199.5 |  |
| NTI21085 |  | 33.919899 | -118.373802 | NORTHROP GRUMMAN CORP | HAWTHORNE, CA | TCA |  |  | 183717.2 |  |
| NTI21086 |  | 33.919899 | -118.319702 | NORTHROP GRUMMAN CO, ELECTRONI | HAWTHORNE, CA | TCA |  |  | 159.3 |  |
| NTI21090 |  | 34.2397995 | -118.400703 | NUPLA CORP | SUN VALLEY, CA | MC | 544.3 |  |  |  |
| NTI21097 |  | 34.2022018 | -118.4217 | ONTIC ENGINEERING & MANUFACTUR | NORTH HOLLYWOOD, CA | TCA |  |  | 143.8 |  |
| NTI21099 |  | 33.889801 | -118.0597 | ORANGE CO. NAME PLATE CO INC | SANTA FE SPRINGS, CA | TCA |  |  | 2382.5 |  |
| NTI21100 |  | 33.8723984 | -118.037903 | ORBIT TESTING INC | CERRITOS, CA | TCA |  |  | 1564.9 |  |
| NTI21101 |  | 34.1790009 | -118.3237 | OROAMERICA | BURBANK, CA | TCA |  |  | 192.4 |  |
| NTI21104 |  | 33.9898987 | -118.212502 | OWENS-BROCKWAY GLASS CONTAINER | VERNON, CA | TCA |  |  | 7809.6 |  |
| NTI21108 |  | 33.9099007 | -118.308701 | P.B. FASTENERS | GARDENA, CA | PCE |  | 459.9 |  |  |
| NTI21110 |  | 34.2011986 | -118.356598 | PACIFIC AIRMOTIVE CORP | BURBANK, CA | TCA |  |  | 8850.8 |  |
| NTI21125 |  | 34.0098991 | -118.266899 | PALACE PLATING | LOS ANGELES, CA | PCE |  | 7728.8 |  |  |
| NTI21139 |  | 33.9986 | -118.147697 | PAULY INC | COMMERCE, CA | TCA |  |  | 2124.6 |  |
| NTI21140 |  | 34.2312012 | -118.487396 | PCA ELECTRONICS INC | SEPULVEDA, CA | TCA |  |  | 2698.9 |  |
| NTI21146 |  | 33.8799019 | -118.275803 | PERMALITE REPROMEDIA CORP | GARDENA, CA | TCA |  |  | 277.1 |  |
| NTI21153 |  | 34.1299019 | -117.9217 | PHAOSTRON INSTRUMENT & ELECTRO | AZUSA, CA | PCE |  | 61.2 |  |  |
| NTI21158 |  | 34.0798988 | -118.343803 | PHYLRICH INTERNATIONAL | LOS ANGELES, CA | TCA |  |  | 3547.5 |  |
| NTI21165 |  | 34.0499001 | -118.040001 | PLASTIC DRESS-UP CO | SOUTH EL MONTE, CA | TCA |  |  | 6833.4 |  |
| NTI21168 |  | 33.9989014 | -117.898598 | PLATO PROD INC | INDUSTRY, CA | PCE |  | 514.4 |  |  |
| NTI21178 |  | 33.7899017 | -118.2313 | PRAXAIR INC | WILMINGTON, CA | TCA |  |  | 2177.2 |  |
| NTI21181 |  | 33.8899002 | -118.048897 | PRECISION TUBE BENDING | SANTA FE SPRINGS, CA | PCE |  | 19586.1 |  |  |
| NTI21182 |  | 33.8919983 | -118.1679 | PREMIUM PLASTICS INC | PARAMOUNT, CA | TCA |  |  | 2380.0 |  |
| NTI21193 |  | 34.2233009 | -118.389503 | PYRAMID POWDER COATING | SUN VALLEY, CA | TCA |  |  | 1382.5 |  |
| NTI21198 |  | 33.9174995 | -118.319603 | QUALITY HARDWARE MFG CO INC | HAWTHORNE, CA | TCA |  |  | 6361.6 |  |
| NTI21203 |  | 34.1945 | -118.389 | R & B AIRCRAFT SUPPLY INC | NORTH HOLLYWOOD, CA | TCA |  |  | 383.2 |  |
| NTI21204 |  | 34.0598984 | -117.975098 | R & G ENAMELING | BALDWIN PARK, CA | TCA |  |  | 12464.7 |  |
| NTI21209 |  | 34.1997986 | -118.400002 | RAINTREE BUCKLES & JEWELRY INC | NORTH HOLLYWOOD, CA | TCA |  |  | 4556.8 |  |
| NTI21210 |  | 34.1299019 | -118.2687 | RALPHS GROCERY CO | LOS ANGELES, CA | TCA |  |  | 1.3 |  |
| NTI21216 |  | 33.9880981 | -118.299103 | RAPID INDUSTRIES | LOS ANGELES, CA | TCA |  |  | 124.7 |  |
| NTI21219 |  | 33.9698982 | -118.049896 | RASMUSSEN IRON WORKS INC | WHITTIER, CA | TCA |  |  | 1362.1 |  |
| NTI21224 |  | 33.9799004 | -118.125801 | RELIABLE METALLURGICAL PROCESS | MONTEBELLO, CA | TCA |  |  | 141.0 |  |
| NTI21226 |  | 34.2033005 | -118.410896 | REMO INC | NORTH HOLLYWOOD, CA | MC,TCA | 758.6 |  | 1132.8 |  |
| NTI21228 |  | 33.8723984 | -118.037903 | REVERE TRANSDUCERS INC | CERRITOS, CA | TCA |  |  | 2809.6 |  |
| NTI21235 |  | 34.0499001 | -117.996696 | ROBERT H. PETERSON CO | INDUSTRY, CA | MC | 300.1 |  |  |  |
| NTI21236 |  | 33.9962997 | -118.288399 | ROBERT M. HADLEY CO INC | LOS ANGELES, CA | MC,PCE,TCA | 217.7 | 95.7 | 353.3 |  |
| NTI21238 |  | 33.8002014 | -118.328598 | ROBINSON HELICOPTER CO | TORRANCE, CA | TCA |  |  | 4556.3 |  |
| NTI21249 |  | 34.0166016 | -118.0504 | ROSE HILLS MEM PARK ASSOC | WHITTIER, CA | PCE |  | 10.8 |  |  |
| NTI21250 |  | 34.0199013 | -118.245399 | ROY E. HANSON JR MFG CO | LOS ANGELES, CA | TCA |  |  | 19958.1 |  |
| NTI21255 |  | 34.1330986 | -117.9217 | RUBBER/URETHANES INCORPORATED | AZUSA, CA | PCE |  | 1753.1 |  |  |
| NTI21267 |  | 33.8799019 | -118.286598 | SANI-TOP INC | GARDENA, CA | PCE,TCA |  | 694.4 | 412.3 |  |
| NTI21276 |  | 34.0499992 | -118.050797 | SEACHROME CORP | SOUTH EL MONTE, CA | TCA |  |  | 4136.8 |  |
| NTI21281 |  | 34.026001 | -118.375504 | SEE'S CANDY SHOPS INC | LOS ANGELES, CA | PCE |  | 121.0 |  |  |
| NTI21282 |  | 34.1997986 | -118.345703 | SENIOR FLEXONICS INC/STAINLESS | BURBANK, CA | PCE |  | 5599.8 |  |  |
| NTI21295 |  | 33.8454018 | -118.318497 | SHINTOM WEST CORP OF AMERICA | TORRANCE, CA | TCA |  |  | 219.1 |  |
| NTI21304 |  | 34.0583 | -117.780098 | SIMPSON PAPER CO @ COGEN UNIT | POMONA, CA | TCA |  |  | 3262.7 |  |
| NTI21325 |  | 34.1235008 | -117.986702 | SOUTHWEST PRODUCTS CO | IRWINDALE, CA | TCA |  |  | 1167.7 |  |
| NTI21332 |  | 33.9202003 | -118.406197 | SPECTRUM METAL FINISHERS INC | EL SEGUNDO, CA | TCA |  |  | 1433.9 |  |
| NTI21339 |  | 33.9799004 | -118.255699 | STANDARD NICKEL CHROMIUM PLATI | LOS ANGELES, CA | PCE |  | 20164.9 |  |  |
| NTI21350 |  | 33.8998985 | -118.308502 | STONE MFG CO | GARDENA, CA | MC,PCE,TCE | 458.1 | 322.5 |  | 68.5 |
| NTI21359 |  | 34.1021996 | -117.823898 | SUN BADGE CO | SAN DIMAS, CA | TCA |  |  | 956.6 |  |
| NTI21365 |  | 34.0199013 | -117.974701 | SUNSET FIREPLACE FIXTURES INC | INDUSTRY, CA | PCE |  | 5864.9 |  |  |
| NTI21368 |  | 34.1968002 | -118.345703 | SURFACE FINISHING INC | BURBANK, CA | TCA |  |  | 10623.6 |  |
| NTI21373 |  | 33.8979988 | -118.286903 | T & V IND INC | GARDENA, CA | TCA |  |  | 667.5 |  |
| NTI21378 |  | 34.139801 | -118.366501 | TECHNICOLOR INC | NORTH HOLLYWOOD, CA | PCE,TCA |  | 8651.8 | 30023.7 |  |
| NTI21381 |  | 34 | -117.931099 | TELEDYNE CAST PARTS-INDUSTRY O | INDUSTRY, CA | TCA |  |  | 821.0 |  |
| NTI21382 |  | 34.0321999 | -118.462196 | TELEDYNE CONTROLS, DIV TELEDYN | LOS ANGELES, CA | TCA |  |  | 4343.6 |  |
| NTI21383 |  | 34.2356987 | -118.5634 | TELEDYNE ELECTRONIC SYSTEMS | NORTHRIDGE, CA | TCA |  |  | 438.2 |  |
| NTI21384 |  | 33.9098015 | -118.319504 | TELEDYNE IND.INC, TELEDYNE REL | HAWTHORNE, CA | TCA |  |  | 5395.0 |  |
| NTI21385 |  | 33.9830017 | -118.428902 | TELEDYNE MICROELECTRONICS UNIT | LOS ANGELES, CA | TCA |  |  | 3065.0 |  |
| NTI21406 |  | 33.9169998 | -118.189796 | THE GADGET MFG CO | LYNWOOD, CA | TCA |  |  | 272.2 |  |
| NTI21407 |  | 34.0199013 | -118.461998 | THE GILLETTE CO, PAPER MATE GR | SANTA MONICA, CA | PCE |  | 2090.2 |  |  |
| NTI21429 |  | 34.0197983 | -118.234596 | TIMES MIRROR CO, LOS ANGELES T | LOS ANGELES, CA | PCE,TCA |  | 25.1 | 25.1 |  |
| NTI21431 |  | 33.9253998 | -118.168297 | TITAN IND | SOUTH GATE, CA | TCA |  |  | 1796.2 |  |
| NTI21439 |  | 33.9398994 | -118.417397 | TRANS WORLD AIRLINES INC | LOS ANGELES, CA | MC,TCA | 1.8 |  | 6.4 |  |
| NTI21440 |  | 33.9776001 | -118.428802 | TRANSACTION TECH INC | LOS ANGELES, CA | TCA |  |  | 1243.6 |  |
| NTI21441 |  | 34.0119019 | -118.169502 | TRANSDIGM INC, ADEL WIGGINS GR | LOS ANGELES, CA | TCA |  |  | 2485.7 |  |
| NTI21444 |  | 34.0143013 | -118.202003 | TRIANGLE BRASS MFG CO | LOS ANGELES, CA | TCA |  |  | 6319.0 |  |
| NTI21445 |  | 33.9889984 | -118.212502 | TRICO INDUSTRIES INC. | HUNTINGTON PARK, CA | MC,TCA | 1637.9 |  | 12360.6 |  |
| NTI21447 |  | 33.8946991 | -118.1679 | TRIPROCESS CO INC | PARAMOUNT, CA | TCA |  |  | 115.5 |  |
| NTI21450 |  | 34.1099014 | -118.246696 | TRU CUT INC | LOS ANGELES, CA | PCE |  | 886.7 |  |  |
| NTI21463 |  | 34.0130997 | -117.920403 | U S TSUBAKI INC | INDUSTRY, CA | PCE,TCA |  | 0.1 | 0.1 |  |
| NTI21478 |  | 34.2033997 | -118.400002 | UNITED AERONAUTICAL CORP | NORTH HOLLYWOOD, CA | MC | 469.6 |  |  |  |
| NTI21488 |  | 34.1297989 | -118.366302 | UNIVERSAL STUDIOS INC (EIS USE | UNIVERSAL CITY, CA | TCA |  |  | 49.5 |  |
| NTI21499 |  | 33.7499008 | -118.230698 | US GOVT, NAVY DEPT LB SHIPYARD | LONG BEACH, CA | PCE,TCA |  | 80.7 | 6448.7 |  |
| NTI21507 |  | 34.0399017 | -118.050697 | VACCO INDUSTRIES | SOUTH EL MONTE, CA | TCA |  |  | 2978.7 |  |
| NTI21508 |  | 34.226799 | -118.552399 | VALIDYNE ENGINEERING CORP | NORTHRIDGE, CA | TCA |  |  | 472.7 |  |
| NTI21511 |  | 34.3045006 | -118.466904 | VALLEY TODECO CO, DIV LAMSON & | SYLMAR, CA | PCE,TCA |  | 50884.0 | 1115.4 |  |
| NTI21516 |  | 33.7999001 | -118.296204 | VARIAN SAMPLE PREPARATION PROD | HARBOR CITY, CA | MC | 1728.2 |  |  |  |
| NTI21518 |  | 34.1040993 | -117.813004 | VEMCO CORP | SAN DIMAS, CA | TCA |  |  | 6318.1 |  |
| NTI21520 |  | 34.1399002 | -118.279701 | VICKERS INC, STERER DIVISION | LOS ANGELES, CA | TCA |  |  | 5093.8 |  |
| NTI21526 |  | 34.1595001 | -118.290802 | W & F MFG INC | GLENDALE, CA | TCA |  |  | 1799.0 |  |
| NTI21531 |  | 33.892601 | -118.286797 | WALTCO ENGINEERING CO | GARDENA, CA | TCA |  |  | 97622.1 |  |
| NTI21544 |  | 34.276001 | -118.4338 | WELCH METAL PROD. INC | SAN FERNANDO, CA | MC,TCA | 400.5 |  | 1525.8 |  |
| NTI21565 |  | 34.1999016 | -118.410797 | WHITTAKER CONTROLS INC | NORTH HOLLYWOOD, CA | TCA |  |  | 5504.8 |  |
| NTI21573 |  | 33.9999008 | -118.125999 | WOLFER PRINTING CO | COMMERCE, CA | PCE |  | 32.0 |  |  |
| NTI21575 |  | 34.1040001 | -118.246597 | WONTRONICS INC | LOS ANGELES, CA | TCA |  |  | 1007.0 |  |
| NTI21646 |  | 37.9472008 | -122.4879 | LUCAS DIGITAL LTD LLC | SAN RAFAEL, CA | TCA |  |  | 377.6 |  |
| NTI21834 |  | 36.6559982 | -121.635101 | LANTIS CORP | SALINAS, CA | TCA |  |  | 2618.6 |  |
| NTI21943 |  | 33.7099991 | -117.841698 | A. C. D. INC | SANTA ANA, CA | TCA |  |  | 11431.9 |  |
| NTI21958 |  | 33.8530006 | -117.8647 | ALL-BANN ENTER. INC | ANAHEIM, CA | TCA |  |  | 5375.2 |  |
| NTI21961 |  | 33.8599014 | -117.897202 | AMERICAN ELECTRONICS INC | FULLERTON, CA | PCE |  | 1627.9 |  |  |
| NTI21976 |  | 33.7064018 | -117.928001 | AST RESEARCH INC | FOUNTAIN VALLEY, CA | TCA |  |  | 2986.2 |  |
| NTI21981 |  | 33.6999016 | -117.992599 | B & B ENAMELING INC | HUNTINGTON BEACH, CA | TCA |  |  | 2591.4 |  |
| NTI21988 |  | 33.8619995 | -117.864799 | BASF STRUCTURAL MATERIALS INC | ANAHEIM, CA | TCA |  |  | 572.9 |  |
| NTI21991 |  | 33.7770996 | -118.004303 | BAZZ-HOUSTON CO | GARDEN GROVE, CA | PCE |  | 11138.9 |  |  |
| NTI21992 |  | 33.9263992 | -117.941101 | BECKMAN INSTRUMENTS INC (EIS & | FULLERTON, CA | TCA |  |  | 10728.8 |  |
| NTI22010 |  | 33.8779984 | -117.8974 | CALIFORNIA STATE UNIVERSITY, F | FULLERTON, CA | PCE,TCA |  | 0.1 | 0.1 |  |
| NTI22012 |  | 33.6492004 | -117.722504 | CALSONIC CLIMATE CONTROL INC | IRVINE, CA | TCA |  |  | 5222.4 |  |
| NTI22014 |  | 33.6800003 | -117.8629 | CANON BUSINESS MACHINES INC | COSTA MESA, CA | TCA |  |  | 2491.6 |  |
| NTI22017 |  | 33.669899 | -117.873596 | CERADYNE INC | COSTA MESA, CA | TCA |  |  | 2683.6 |  |
| NTI22022 |  | 33.8596992 | -117.810699 | CIBA-GEIGY CORP, COMPOSITE MAT | ANAHEIM, CA | TCA |  |  | 102.5 |  |
| NTI22029 |  | 33.8614998 | -117.810699 | CONTROL DATA CORPORATION | ANAHEIM, CA | TCA |  |  | 836.0 |  |
| NTI22035 |  | 33.8098984 | -117.896698 | CREST COATING INC | ANAHEIM, CA | TCA |  |  | 7363.6 |  |
| NTI22045 |  | 33.7999001 | -117.864098 | DESIGNS ALIVE INC | ORANGE, CA | PCE,TCA |  | 5.4 | 5.4 |  |
| NTI22048 |  | 33.634201 | -117.938004 | EATON CORPORATION, MSC PRODUCT | COSTA MESA, CA | MC,TCA | 25.4 |  | 3515.8 |  |
| NTI22049 |  | 33.8498993 | -117.843002 | ECONOLITE CONTROL PRODUCTS, IN | ANAHEIM, CA | TCA |  |  | 5195.9 |  |
| NTI22051 |  | 33.8498993 | -117.843002 | ELECTRO METAL FINISHING CORPOR | ANAHEIM, CA | TCA |  |  | 8794.7 |  |
| NTI22055 |  | 33.705101 | -117.863197 | ELPAC ELECTRONICS INC | SANTA ANA, CA | TCA |  |  | 2653.6 |  |
| NTI22058 |  | 33.6836014 | -117.8414 | EVEREST ELECTRONIC EQUIP INC | ANAHEIM, CA | TCA |  |  | 1114.6 |  |
| NTI22060 |  | 33.7145996 | -117.917198 | EXPRESS MFG INC | SANTA ANA, CA | TCA |  |  | 3251.8 |  |
| NTI22062 |  | 33.7201004 | -117.917297 | FAIRCHILD FASTENER GROUP,ROSAN | SANTA ANA, CA | TCA |  |  | 2085.6 |  |
| NTI22065 |  | 33.7098999 | -117.863197 | FILTER CONCEPTS INC | SANTA ANA, CA | TCA |  |  | 1214.7 |  |
| NTI22066 |  | 33.7127991 | -117.928001 | FIRE PLACE MFG INC | SANTA ANA, CA | PCE,TCA |  | 0.6 | 1052.9 |  |
| NTI22067 |  | 33.7421989 | -117.971497 | FLETCHER ENGINEERING INC | WESTMINSTER, CA | PCE |  | 684.7 |  |  |
| NTI22074 |  | 33.8530998 | -117.853897 | FURON CO | ANAHEIM, CA | TCA |  |  | 7239.3 |  |
| NTI22087 |  | 33.6299019 | -117.937897 | GULTON STATHAM TRANSDUCERS | COSTA MESA, CA | TCA |  |  | 7671.2 |  |
| NTI22091 |  | 33.8067017 | -117.907402 | HARDIN MARINE | ANAHEIM, CA | TCA |  |  | 956.6 |  |
| NTI22094 |  | 33.7258987 | -117.8526 | HIGH-TECH COATINGS | SANTA ANA, CA | TCA |  |  | 1496.9 |  |
| NTI22099 |  | 33.6299019 | -117.927101 | HUGHES AIRCRAFT CO, MICROELECT | NEWPORT BEACH, CA | TCA |  |  | 1349.9 |  |
| NTI22106 |  | 33.8219986 | -117.918404 | INTERSTATE ELECTRONICS CORP | ANAHEIM, CA | TCA |  |  | 967.5 |  |
| NTI22111 |  | 33.8498993 | -117.8647 | J. G. & T. QUALITY SPRAY PAINT | ANAHEIM, CA | TCA |  |  | 10408.6 |  |
| NTI22112 |  | 33.7198982 | -117.8526 | J.L. WOOD OPTICAL SYS | SANTA ANA, CA | TCA |  |  | 1333.8 |  |
| NTI22117 |  | 33.8599014 | -117.897202 | JOHNSON CONTROLS BATTERY GROUP | FULLERTON, CA | MC,TCA | 640.0 |  | 634.6 |  |
| NTI22118 |  | 33.7126999 | -117.938797 | KAGA INC | FOUNTAIN VALLEY, CA | TCA |  |  | 8064.4 |  |
| NTI22119 |  | 33.6898994 | -117.852303 | KAISER ELECTROPRECISION | IRVINE, CA | TCA |  |  | 26233.5 |  |
| NTI22124 |  | 33.8456001 | -118.005096 | KNOTT'S BERRY FARM | BUENA PARK, CA | PCE,TCA |  | 4.5 | 4.5 |  |
| NTI22126 |  | 33.8298988 | -117.9077 | KWIKSET CORP | ANAHEIM, CA | PCE |  | 16174.2 |  |  |
| NTI22138 |  | 33.8493996 | -117.864601 | LITE CTR OF CAL | ANAHEIM, CA | TCA |  |  | 30.6 |  |
| NTI22144 |  | 33.8184013 | -117.9076 | MAGNETEK | ANAHEIM, CA | TCA |  |  | 5554.5 |  |
| NTI22160 |  | 33.8627014 | -117.897202 | MICRODOT INC, KAYNAR MANUFACTU | FULLERTON, CA | PCE |  | 54196.6 |  |  |
| NTI22162 |  | 33.7098999 | -117.906403 | MICROSEMI CORP | SANTA ANA, CA | TCA |  |  | 778.4 |  |
| NTI22176 |  | 33.7081985 | -117.938797 | NEWPORT ADHESIVE INC | FOUNTAIN VALLEY, CA | MC | 7620.4 |  |  |  |
| NTI22180 |  | 33.7960014 | -118.004501 | OCA APPLIED OPTICS INC | GARDEN GROVE, CA | TCA |  |  | 1953.2 |  |
| NTI22181 |  | 33.7098999 | -117.852501 | ONE WAY MFG | SANTA ANA, CA | TCA |  |  | 2199.5 |  |
| NTI22183 |  | 33.8599014 | -117.897202 | OR. CO. PAINTING | FULLERTON, CA | TCA |  |  | 7983.2 |  |
| NTI22191 |  | 33.6898994 | -117.841499 | PACKARD HUGHES INTERCONNECT | IRVINE, CA | TCA |  |  | 823.7 |  |
| NTI22192 |  | 33.669899 | -117.841301 | PARKER HANNIFIN AEROSPACE CORP | IRVINE, CA | PCE |  | 22588.9 |  |  |
| NTI22207 |  | 33.6954002 | -117.830704 | PROGRAM DATA INC | IRVINE, CA | MC,TCA | 25.1 |  | 110.0 |  |
| NTI22209 |  | 33.6954994 | -117.949402 | PSITECH | FOUNTAIN VALLEY, CA | TCA |  |  | 136.1 |  |
| NTI22210 |  | 33.7078018 | -117.863197 | QED INC. | SANTA ANA, CA | TCA |  |  | 1337.2 |  |
| NTI22222 |  | 33.669899 | -117.873596 | ROCKWELL INTERNATIONAL COLLINS | COSTA MESA, CA | TCA |  |  | 170.6 |  |
| NTI22239 |  | 33.6806984 | -117.873703 | SEMICOA | COSTA MESA, CA | TCA |  |  | 224.5 |  |
| NTI22241 |  | 33.8599014 | -117.810699 | SETCO INC | ANAHEIM, CA | TCA |  |  | 1938.4 |  |
| NTI22253 |  | 33.7398987 | -118.003899 | SO CAL EDISON CO (EIS USE) | WESTMINSTER, CA | TCA |  |  | 160.6 |  |
| NTI22254 |  | 33.8610992 | -117.864799 | SONFARREL INC | ANAHEIM, CA | MC | 274.8 |  |  |  |
| NTI22255 |  | 33.6917 | -117.852303 | SORIN BIOMEDICAL INC | IRVINE, CA | MC,TCA | 283.0 |  | 1618.4 |  |
| NTI22259 |  | 33.7198982 | -117.8526 | SPEEDWAY METAL FINISHING | SANTA ANA, CA | PCE |  | 214.2 |  |  |
| NTI22260 |  | 33.7127991 | -117.928001 | SPS TECHNOLOGIES INC | SANTA ANA, CA | MC,TCA | 480.5 |  | 5488.5 |  |
| NTI22271 |  | 33.7074013 | -117.917198 | SURVIVAIR, A DIV OF COMASEC IN | SANTA ANA, CA | TCA |  |  | 272.2 |  |
| NTI22277 |  | 33.8098984 | -117.950699 | TAYLOR-DUNN MFG CO | ANAHEIM, CA | TCA |  |  | 63.4 |  |
| NTI22280 |  | 33.5550995 | -117.775497 | TELONIC BERKELEY INC | LAGUNA BEACH, CA | TCA |  |  | 490.3 |  |
| NTI22288 |  | 33.8599014 | -117.821503 | THE HARTWELL CORP | PLACENTIA, CA | TCA |  |  | 1882.4 |  |
| NTI22292 |  | 33.8098984 | -117.864197 | THERMCO SYSTEMS CORP | ORANGE, CA | TCA |  |  | 522.5 |  |
| NTI22295 |  | 33.7298012 | -118.036102 | TIODIZE INC | HUNTINGTON BEACH, CA | PCE |  | 2222.6 |  |  |
| NTI22323 |  | 33.7899017 | -117.874802 | VARCO INTL INC. | ORANGE, CA | MC,TCA | 14.5 |  | 801.5 |  |
| NTI22326 |  | 33.7998009 | -118.058601 | VESPER CORP | LOS ALAMITOS, CA | PCE |  | 5740.2 |  |  |
| NTI22330 |  | 33.8098984 | -117.9291 | WCO HOTELS INC | ANAHEIM, CA | TCA |  |  | 1.0 |  |
| NTI22332 |  | 33.8599014 | -117.907997 | WEBER AIRCRAFT INC | FULLERTON, CA | TCA |  |  | 11147.2 |  |
| NTI22366 |  | 33.8199005 | -117.270103 | ALPHA/OWENS-CORNING, L.L.C. | PERRIS, CA | MC | 82.1 |  |  |  |
| NTI22372 |  | 33.6505013 | -116.191299 | ARMTEC DEFENSE PRODUCTS CO | COACHELLA, CA | MC | 1346.9 |  |  |  |
| NTI22375 |  | 33.8656998 | -117.259399 | AURORA MODULAR INDUSTRIES INC | PERRIS, CA | PCE,TCA |  | 0.9 | 0.9 |  |
| NTI22379 |  | 34.0008011 | -117.346497 | BOURNS INC | RIVERSIDE, CA | TCA |  |  | 3964.4 |  |
| NTI22429 |  | 33.8799019 | -117.540604 | METRO LINE INDUSTRIES, INC, R. | CORONA, CA | TCA |  |  | 743.2 |  |
| NTI22430 |  | 33.839901 | -117.5187 | MINNESOTA MINING & MFG CO | CORONA, CA | TCA |  |  | 79.3 |  |
| NTI22458 |  | 33.9398994 | -117.465202 | ROHR,INC | RIVERSIDE, CA | TCA |  |  | 26734.7 |  |
| NTI22470 |  | 33.8816986 | -117.594704 | TRANSCHEM, JETRONICS IND INC D | CORONA, CA | TCA |  |  | 2490.2 |  |
| NTI22474 |  | 33.8899994 | -117.248703 | US GOVT, AF DEPT, MARCH AFB (N | RIVERSIDE, CA | MC,TCA | 736.6 |  | 3166.1 |  |
| NTI22477 |  | 33.9698982 | -117.367996 | WESTERN POLYFORM CORP | RIVERSIDE, CA | TCA |  |  | 6486.0 |  |
| NTI22485 |  | 38.6310043 | -121.213905 | AEROJET | RANCHO CORDOVA, CA | MC,PCE,TCA,TCE | 4439.6 | 230.5 | 37710.9 | 42.7 |
| NTI22495 |  | 38.5248985 | -121.394096 | APPARATUS UNLIMITED, INC. | SACRAMENTO, CA | TCA |  |  | 830.9 |  |
| NTI22624 |  | 38.4486008 | -121.4645 | REGIONAL SANITATION DIST | ELK GROVE, CA | MC,PCE,TCA,TCE | 0.9 | 1.4 | 1.4 | 0.9 |
| NTI22632 |  | 38.5140991 | -121.394302 | SACRAMENTO ARMY DEPOT | SACRAMENTO, CA | MC,TCA | 580.6 |  | 332.6 |  |
| NTI22652 |  | 38.5946007 | -121.495903 | STATE OF CALIF PRINTING | SACRAMENTO, CA | PCE,TCA |  | 529.8 | 110.2 |  |
| NTI22676 |  | 38.5929985 | -121.495903 | WEMCO | SACRAMENTO, CA | TCA |  |  | 8904.5 |  |
| NTI22709 |  | 34 | -117.671303 | AMERICAN EAGLE WHEEL CORPORATI | CHINO, CA | TCA |  |  | 27151.1 |  |
| NTI22710 |  | 34.0298996 | -117.519897 | AMERICAN SECURITY PRODUCTS CO | FONTANA, CA | TCA |  |  | 7303.7 |  |
| NTI22720 |  | 34.0800018 | -117.541901 | ARLON ELECTRONICS SUBSTRATES D | RANCHO CUCAMONGA, CA | TCA |  |  | 2520.8 |  |
| NTI22733 |  | 34 | -117.703796 | BRIGHT SHARK POWDER COATING | CHINO, CA | TCA |  |  | 3630.6 |  |
| NTI22744 |  | 34.0699005 | -117.5093 | CALIFORNIA STEEL INDUSTRIES IN | FONTANA, CA | MC,PCE,TCA | 2077.9 | 0.5 | 0.1 |  |
| NTI22774 |  | 34.0798988 | -117.281799 | FRANKLIN PRESS | SAN BERNARDINO, CA | TCA |  |  | 5.3 |  |
| NTI22776 |  | 34.0598984 | -117.541702 | FRUIT GROWERS SUPPLY CO | ONTARIO, CA | TCA |  |  | 35.4 |  |
| NTI22787 |  | 34.089901 | -117.5961 | GOODYEAR RUBBER CO,GOODYEAR RU | RANCHO CUCAMONGA, CA | TCA |  |  | 5887.6 |  |
| NTI22816 |  | 34.0499992 | -117.195 | LA-Z-BOY WEST | REDLANDS, CA | TCA |  |  | 1044.6 |  |
| NTI22824 |  | 34.0399017 | -117.639099 | LOUD ENGINEERING & MFG INC | ONTARIO, CA | TCA |  |  | 3419.9 |  |
| NTI22848 |  | 35.6493988 | -117.530197 | NAVAL WEAPONS CENTER | CHINA LAKE, CA | MC | 538.5 |  |  |  |
| NTI22866 |  | 34.0598984 | -117.541702 | PRAXAIR INC | ONTARIO, CA | TCA |  |  | 544.3 |  |
| NTI22907 |  | 34.0578995 | -117.693398 | SPRAYLINE ENTER. INC | ONTARIO, CA | MC,TCA | 44.9 |  | 3066.7 |  |
| NTI22925 |  | 34.0084 | -117.065002 | THE J. M. NEY CO | YUCAIPA, CA | TCA |  |  | 1039.6 |  |
| NTI22927 |  | 34.0600014 | -117.552597 | THERMAL DYNAMICS CORP | ONTARIO, CA | TCA |  |  | 19776.6 |  |
| NTI22939 |  | 34.2312012 | -116.055496 | USMC A/G COMBAT CENTER | TWENTYNINE PALMS, CA | PCE,TCA |  | 20.7 | 142.9 |  |
| NTI22940 |  | 34.8750992 | -116.912498 | USMC LOGISTICS BASE - NEBO |  | PCE,TCA |  | 99.8 | 99.8 |  |
| NTI22941 |  | 34.8823471 | -116.885323 | USMC LOGISTICS BASE - YERMO | BARSTOW, CA | MC,PCE,TCA | 123.8 | 38173.4 | 2693.7 |  |
| NTI22952 |  | 34.0924988 | -117.639503 | WESTERN MOULDINGS | UPLAND, CA | PCE |  | 38101.8 |  |  |
| NTI23064 |  | 32.8210678 | -117.142349 | KYOCERA AMERICA INC. | SAN DIEGO, CA | MC,PCE,TCA | 0.0 | 0.0 | 0.0 |  |
| NTI23077 |  | 32.6908569 | -117.13282 | NATIONAL STEEL & SHIPBUILDING | SAN DIEGO, CA | MC,PCE,TCA | 1.2 | 9.6 | 22.7 |  |
| NTI23188 |  | 33.3189354 | -117.372543 | USMC BASE / CAMP PENDLETON | CAMP PENDLETON, CA | MC,PCE,TCA | 8.2 | 13.6 | 13.6 |  |
| NTI23392 |  | 37.7747993 | -122.420898 | MONACO LABORATORIES INC | SAN FRANCISCO, CA | TCA |  |  | 7438.0 |  |
| NTI23404 |  | 37.7476006 | -122.398499 | O'NEILL INC | SAN FRANCISCO, CA | TCA |  |  | 99.2 |  |
| NTI23510 |  | 37.6367989 | -122.399399 | UNITED AIRLINES, MAINTENANCE O | SAN FRANCISCO, CA | TCA |  |  | 47850.5 |  |
| NTI23514 |  | 37.7703018 | -122.432297 | UNITED STATES MINT | SAN FRANCISCO, CA | PCE |  | 41.6 |  |  |
| NTI23615 |  | 37.8554001 | -121.272301 | DDRW - SHARPE SITE | LATHROP, CA | TCA |  |  | 541.1 |  |
| NTI23692 |  | 37.7141991 | -121.491096 | OWENS-BROCKWAY GLASS CONTAINER | TRACY, CA | TCA |  |  | 12294.2 |  |
| NTI24080 |  | 37.5668983 | -122.320702 | DURA FINISH OF SAN MATEO | SAN MATEO, CA | MC | 484.0 |  |  |  |
| NTI24167 |  | 37.5051994 | -122.253304 | LITTON ELECTRON DEVICES DIVISI | SAN CARLOS, CA | TCA |  |  | 3.0 |  |
| NTI24183 |  | 37.4752998 | -122.219704 | METAL FUSION INC | REDWOOD CITY, CA | TCA |  |  | 144.6 |  |
| NTI24285 |  | 37.389801 | -122.243202 | STANFORD LINEAR ACCELERATOR | MENLO PARK, CA | TCA |  |  | 1756.1 |  |
| NTI24352 |  | 34.9110489 | -120.450119 | ARROW AUTOMOTIVE INDUSTRIES | SANTA MARIA, CA | TCA |  |  | 0.0 |  |
| NTI24404 |  | 34.9152985 | -120.460503 | LUCAS AVIATION - SANTA MARIA | SANTA MARIA, CA | TCA |  |  | 1538.6 |  |
| NTI24409 |  | 34.4188004 | -119.698402 | PACIFIC SCIENTIFIC | SANTA BARBARA, CA | TCA |  |  | 2424.1 |  |
| NTI24426 |  | 34.4309998 | -119.873001 | SBRC - BUILDING 21 | GOLETA, CA | MC,TCA | 198.2 |  | 517.1 |  |
| NTI24427 |  | 34.9225006 | -120.460297 | SBRC - BUILDING 50 - SANTA MAR | SANTA MARIA, CA | MC,PCE,TCA | 17.6 | 49.4 | 3856.2 |  |
| NTI24430 |  | 34.4309998 | -119.873001 | SBRC - BUILDINGS 20/30/32 - HO | GOLETA, CA | MC,TCA | 235.9 |  | 487.2 |  |
| NTI24506 |  | 37.2983017 | -121.849197 | APTEK INC | SAN JOSE, CA | TCA |  |  | 706.3 |  |
| NTI24529 |  | 37.3605003 | -121.9048 | BABBITT BEARING CO INC | SAN JOSE, CA | MC | 45.2 |  |  |  |
| NTI24720 |  | 37.3865013 | -122.039902 | ENDEVCO | SUNNYVALE, CA | TCA |  |  | 9.1 |  |
| NTI24722 |  | 37.2857552 | -121.940544 | ETCHED MEDIA CORPORATION | CAMPBELL, CA | TCA |  |  | 956.0 |  |
| NTI24755 |  | 37.3625412 | -121.949158 | FMG ENTERPRISES INC | SANTA CLARA, CA | PCE |  | 339.1 |  |  |
| NTI24758 |  | 37.4045982 | -121.938004 | FOXBORO/ICT | SAN JOSE, CA | TCA |  |  | 491.2 |  |
| NTI24796 |  | 37.3829994 | -121.9496 | HEDB CORPORATION | SANTA CLARA, CA | TCA |  |  | 158.0 |  |
| NTI24823 |  | 37.2015991 | -121.828201 | IBM CORP, RESEARCH FACILITIES | SAN JOSE, CA | MC | 6.0 |  |  |  |
| NTI24824 |  | 37.2482986 | -121.804901 | IBM CORPORATION | SAN JOSE, CA | TCA |  |  | 96.3 |  |
| NTI24980 |  | 37.3888016 | -122.107697 | NASA-AMES RESEARCH CENTER | MOUNTAIN VIEW, CA | MC | 0.5 |  |  |  |
| NTI25016 |  | 37.2748985 | -121.951103 | PACIFIC AEROSPACE SERVICES | CAMPBELL, CA | TCA,TCE |  |  | 1086.8 | 193.7 |
| NTI25038 |  | 37.4102287 | -121.894287 | PECO CONTROLS CORP | MILPITAS, CA | TCA,TCE |  |  | 17.2 | 304.2 |
| NTI25045 |  | 37.3349991 | -122.029297 | PG&E CUPERTINO SERVICE CENTER | CUPERTINO, CA | TCA |  |  | 12.3 |  |
| NTI25148 |  | 37.401413 | -121.915611 | SENSYM | MILPITAS, CA | TCA |  |  | 0.0 |  |
| NTI25212 |  | 37.386055 | -122.03228 | SUNPOWER CORPORATION | SUNNYVALE, CA | TCA |  |  | 9.1 |  |
| NTI25216 |  | 37.4046135 | -122.024239 | SUPERTEX, INC | SUNNYVALE, CA | TCA |  |  | 0.5 |  |
| NTI25245 |  | 37.3764992 | -122.028702 | TOBAR INDUSTRIES | MOUNTAIN VIEW, CA | MC | 150.4 |  |  |  |
| NTI25264 |  | 37.2332993 | -121.748802 | UNITED TECHNOLOGIES CORPORATIO | SAN JOSE, CA | TCA |  |  | 644.1 |  |
| NTI25296 |  | 37.398201 | -122.152702 | WATKINS-JOHNSON COMPANY | PALO ALTO, CA | MC | 2.5 |  |  |  |
| NTI25481 |  | 38.2429733 | -122.039009 | OEA AREOSPACE INC | FAIRFIELD, CA | TCA |  |  | 152.3 |  |
| NTI25515 |  | 38.2464981 | -121.960098 | TRAVIS AFB | TRAVIS AFB, CA | MC | 41.1 |  |  |  |
| NTI25648 |  | 38.4758987 | -122.6446 | MICROSOURCE, INC | SANTA ROSA, CA | TCA |  |  | 3.0 |  |
| NTI25756 |  | 38.4309998 | -122.7136 | ZUMWALT MAGRINI CHRYSLER | SANTA ROSA, CA | MC | 55.3 |  |  |  |
| NTI25972 |  | 34.1632996 | -119.223801 | ANACAPA MARINE SERVICE | OXNARD, CA | MC,PCE,TCA | 0.1 | 1.1 | 1.0 |  |
| NTI25980 |  | 34.2498016 | -119.226097 | BELL POWDER COATING | VENTURA, CA | MC,TCA | 528.9 |  | 2931.6 |  |
| NTI25984 |  | 34.1469002 | -119.18 | BMW - VEHICLE PREPARATION | OXNARD, CA | MC | 63.2 |  |  |  |
| NTI26000 |  | 34.2052002 | -119.149002 | ERG INTERNATIONAL | OXNARD, CA | TCA |  |  | 530.0 |  |
| NTI26004 |  | 34.2209015 | -119.073402 | G & H TECHNOLOGY | CAMARILLO, CA | TCA |  |  | 150.4 |  |
| NTI26005 |  | 34.2498016 | -119.226097 | GENERAL MAGNAPLATE CALIF. | VENTURA, CA | TCA |  |  | 2093.7 |  |
| NTI26006 |  | 34.2817001 | -118.879303 | GENERAL OPTICS, INC. | MOORPARK, CA | TCA |  |  | 3120.4 |  |
| NTI26014 |  | 34.1449013 | -119.190804 | HUENEME BOAT WORKS | PORT HUENEME, CA | MC | 22.5 |  |  |  |
| NTI26022 |  | 34.289299 | -118.857803 | KAVLICO CORPORATION | MOORPARK, CA | TCA |  |  | 9310.4 |  |
| NTI26038 |  | 34.2697983 | -118.705299 | NATEL ENGINEERING | SIMI VALLEY, CA | MC,TCA | 24.9 |  | 2582.8 |  |
| NTI26056 |  | 34.1907005 | -118.931602 | PTI TECHNOLOGIES INC. | NEWBURY PARK, CA | TCA |  |  | 464.2 |  |
| NTI26059 |  | 34.2584 | -119.248001 | ROBERT M. HADLEY CO. INC. | VENTURA, CA | TCA |  |  | 355.9 |  |
| NTI26060 |  | 34.2476006 | -118.683098 | ROCKETDYNE DIVISION | SIMI VALLEY, CA | TCA,TCE |  |  | 11467.0 | 3441.8 |
| NTI26068 |  | 34.2070007 | -119.249901 | SCE-MANDALAY GEN STATION | OXNARD, CA | TCA |  |  | 352.6 |  |
| NTI26069 |  | 34.1237984 | -119.1632 | SCE-ORMOND BEACH GEN STATION |  | TCA |  |  | 528.9 |  |
| NTI26084 |  | 34.2140007 | -119.160004 | ST JOHN'S REGIONAL HOSPITAL | OXNARD, CA | TCA |  |  | 37.4 |  |
| NTI26095 |  | 34.1707001 | -119.158897 | THE TALLEY CORPORATION | OXNARD, CA | PCE,TCA |  | 3.5 | 2060.0 |  |
| NTI26183 |  | 39.1194115 | -75.5667725 | CAMDEL METALS CORPORATION | CAMDEN, DE | TCE |  |  |  | 8344.3 |
| NTI31360 |  | 39.033699 | -84.9679031 | AURORA CASKET CO-VANGUARD PLT | AURORA, IN | TCE |  |  |  | 3075.4 |
| NTI31387 |  | 41.4216995 | -84.8628387 | THERMA-TRU CORPORATION | BUTLER, IN | MC | 3120.7 |  |  |  |
| NTI31541 |  | 41.6739998 | -85.9813004 | FLEXIBLE FOAM PRODUCTS, INC. | ELKHART, IN | MC | 406346.1 |  |  |  |
| NTI32072 |  | 39.7335014 | -86.2111969 | ALLISON ENGINE COMPANY, INC. PLANT 5 & 8 | INDIANAPOLIS, IN | PCE |  | 2267.4 |  |  |
| NTI32786 |  | 39.0239258 | -94.7142715 | VITA CRAFT CORPORATION | SHAWNEE, KS | PCE |  | 13606.9 |  |  |
| NTI32829 |  | 37.6642761 | -97.3833618 | AIR CAPITOL PLATING, INC. | WICHITA, KS | TCE |  |  |  | 12401.2 |
| NTI32831 |  | 37.6244431 | -97.2805557 | BOEING COMMERCIAL AIRPLANE GROUP | WICHITA, KS | PCE,TCE |  | 184067.8 |  | 74570.6 |
| NTI32837 |  | 37.6876984 | -97.3908005 | METAL FINISHING COMPANY |  | TCE |  |  |  | 11675.5 |
| NTI32838 |  | 37.6938896 | -97.2241669 | RAYTHEON AIRCRAFT COMPANY | WICHITA, KS | TCE |  |  |  | 308.4 |
| NTI32870 |  | 37.6810989 | -85.9192963 | AMERICAN BRAKE IND CORP | ELIZABETHTOWN, KY | TCA |  |  | 93342.9 |  |
| NTI33916 |  | 42.8772888 | -85.5674973 | DIESEL TECHNOLOGY COMPANY | KENTWOOD, MI | TCE |  |  |  | 1680.3 |
| NTI34114 |  | 38.9730606 | -92.3052826 | WATLOW COLUMBIA |  | TCE |  |  |  | 1544.5 |
| NTI34145 |  | 38 | -92.75 | MODINE HEAT TRANSFER INC |  | MC,TCA | 19666.9 |  | 695.8 |  |
| NTI34209 |  | 38.9500008 | -92.7333298 | NORDYNE, INC |  | TCE |  |  |  | 8447.7 |
| NTI34210 |  | 38.978611 | -92.9761124 | TOASTMASTER INC |  | TCE |  |  |  | 29312.9 |
| NTI34211 |  | 38.0558281 | -91.4016724 | B.W. FREEEMAN HEEL COMPANY |  | TCA |  |  | 870.9 |  |
| NTI34327 |  | 39.1055603 | -94.2541733 | LAKE CITY ARMY AMMUNITION PLANT |  | TCA |  |  | 2749.2 |  |
| NTI34330 |  | 39.1433983 | -94.5131989 | LIBBY INTERNATIONAL |  | MC | 26.8 |  |  |  |
| NTI34331 |  | 38.9366684 | -94.3911133 | LUCENT TECHNOLOGIES |  | TCE |  |  |  | 249.5 |
| NTI34373 |  | 38.8800011 | -94.5258331 | TOROTEL PRODUCTS INC. |  | TCE |  |  |  | 2696.7 |
| NTI34377 |  | 38.957901 | -94.5753021 | U.S. DEPARTMENT OF ENERGY |  | PCE,TCE |  | 291.7 |  | 8567.0 |
| NTI34385 |  | 37.7655602 | -94.5272217 | EAGLE-PICHER |  | TCE |  |  |  | 4529.1 |
| NTI34395 |  | 37.0602798 | -94.4702835 | MIDCON CABLES COMPANY |  | MC,TCE | 161.5 |  |  | 54.4 |
| NTI34447 |  | 39.6819382 | -91.3566666 | WATLOW INDUSTRIES |  | TCA |  |  | 3640.1 |  |
| NTI34460 |  | 38.8641701 | -91.328331 | UNIQUE AUTOMOTIVE REBUILDERS,INC |  | TCE |  |  |  | 6950.4 |
| NTI34472 |  | 36.0494385 | -94.3583298 | SABRELINER CORPORATION |  | PCE |  | 8847.8 |  |  |
| NTI34486 |  | 37.7458305 | -89.8722229 | TG (USA) CORPORATION |  | TCA |  |  | 5999.9 |  |
| NTI34514 |  | 39.2949982 | -94.6952972 | TRANS WORLD AIRLINES INC |  | PCE |  | 76208.5 |  |  |
| NTI34540 |  | 38.8130608 | -90.7902832 | MCDONNELL DOUGLAS CORPORATION | SAINT CHARLES, MO | TCA |  |  | 9305.0 |  |
| NTI34574 |  | 38.5619392 | -90.4599991 | BOHN & DAWSON INC |  | PCE |  | 2222.6 |  |  |
| NTI34595 |  | 38.5519409 | -90.4605637 | DYNASAUER CORP. |  | MC | 921.7 |  |  |  |
| NTI34632 |  | 38.7583313 | -90.3694382 | MCDONNELL DOUGLAS CORPORATION |  | TCA |  |  | 20.4 |  |
| NTI34673 |  | 38.6100998 | -90.3356018 | SUNNEN PRODUCTS COMPANY |  | PCE |  | 7905.2 |  |  |
| NTI34682 |  | 38.7434006 | -90.3731995 | TRANS WORLD AIRLINES |  | MC,TCA | 1484.3 |  | 2491.5 |  |
| NTI34749 |  | 38.6244011 | -90.2913971 | DRUMTECH, INC. |  | MC | 15327.3 |  |  |  |
| NTI34765 |  | 38.6291695 | -90.2061081 | KOKEN MFG CO. INC. |  | TCE |  |  |  | 122.9 |
| NTI34784 |  | 38.5741692 | -90.2327805 | OTTEN SCREW PRODUCTS |  | PCE |  | 41.9 |  |  |
| NTI34802 |  | 38.5933304 | -90.2600021 | TEMPSET INC |  | TCE |  |  |  | 11402.9 |
| NTI35353 |  | 42.1439018 | -76.0456009 | IBM ENDICOTT FACILITY | ENDICOTT, NY | PCE |  | 722.6 |  |  |
| NTI35612 |  | 42.3088989 | -75.3974991 | AMPHENOL CORP - BENDIX CONNECTOR OPERS | SIDNEY, NY | TCE |  |  |  | 982.0 |
| NTI36095 |  | 40.6688995 | -73.9056015 | ARROW LOCK MANUFACTURING CO | BROOKLYN, NY | TCE |  |  |  | 9642.0 |
| NTI37024 |  | 43.1525002 | -77.7388992 | KODAK ELMGROVE PLANT-APPARATUS DIVISION | ROCHESTER, NY | TCE |  |  |  | 8105.7 |
| NTI38194 |  | 43.1050987 | -75.2136002 | UTICA ALLOYS | UTICA, NY | TCE |  |  |  | 17302.7 |
| NTI38195 |  | 43.0886002 | -75.2506027 | UTICA CUTLERY CO | UTICA, NY | TCE |  |  |  | 12839.8 |
| NTI39761 |  | 40.7033005 | -73.3794022 | LAWRENCE RIPAK FACILITY | WEST BABYLON, NY | PCE |  | 2721.6 |  |  |
| NTI40416 |  | 41.4133301 | -81.7852783 | S.K. WELLMAN CORP. |  | PCE |  | 28122.7 |  |  |
| NTI40507 |  | 41.1394997 | -81.476799 | THOMAS MANUFACTURING CO. | CUYAHOGA FALLS, OH | TCE |  |  |  | 25401.2 |
| NTI40611 |  | 44.6545982 | -123.063202 | Wah Chang | ALBANY, OR | TCA |  |  | 1741.1 |  |
| NTI41338 |  | 34.6872864 | -82.2327271 | KEMET:FOUNTAIN INN | FOUNTAIN INN, SC | MC | 1451.5 |  |  |  |
| NTI41417 |  | 34.768055 | -83.0311661 | SCHLUMBERGER INC | WEST UNION, SC | TCE |  |  |  | 1811.6 |
| NTI41653 |  | 32.8550606 | -96.8639374 | GE ENGINESERVICES--DALLAS LP | DALLAS, TX | TCE |  |  |  | 1328.1 |
| NTI42005 |  | 41.5078125 | -112.019135 | Promontory Plant | Promontory, UT | TCA |  |  | 940.6 |  |
| NTI42445 |  | 39.5601006 | -78.8349991 | ALLEGANY BALLISTICS LABORATORY | ROCKET CENTER, WV | MC | 2793.6 |  |  |  |
| NTI42595 |  | 43.1909981 | -88.7307205 | Applied Molded Products Corporation | WATERTOWN, WI | MC | 2993.7 |  |  |  |
| NTI42671 |  | 44.0802727 | -87.7029114 | FOSTER NEEDLE CO., INC. | MANITOWOC, WI | TCE |  |  |  | 19504.5 |
| NTI42701 |  | 44.8938026 | -87.8955078 | CERA-MITE CORPORATION | OCONTO, WI | TCE |  |  |  | 6168.9 |
| NTI42711 |  | 43.3179665 | -87.9590912 | CERA-MITE CORPORATION | GRAFTON, WI | TCE |  |  |  | 3356.6 |
| NTI42750 |  | 42.7270622 | -87.7908859 | RACINE PLATING CO. | RACINE, WI | TCE |  |  |  | 2540.1 |
| NTI43004 |  | 43.6319618 | -88.7345886 | NATIONAL RIVET & MANUFACTURING COMPANY | WAUPUN, WI | TCE |  |  |  | 3628.7 |
| NTI43015 |  | 43.7824593 | -88.450531 | GIDDINGS & LEWIS AUTOMATION TECHNOLOGY | FOND DU LAC, WI | TCE |  |  |  | 2086.5 |
| NTI43378 |  | 36.1203995 | -86.6934509 | AEROSTRUCTURES CORPORATION, THE | NASHVILLE, TN | TCE |  |  |  | 15076.5 |
| NTI44511 |  | 45.213501 | -93.4113007 | IMI Cornelius Inc | ANOKA, MN | TCE |  |  |  | 3925.8 |
| NTI44700 |  | 35.3187599 | -78.6217728 | MORGANITE INC - CARBON DIVISION | DUNN, NC | TCE |  |  |  | 272.2 |
| NTI44730 |  | 44.9150009 | -93.4156036 | Kangas Enameling | HOPKINS, MN | TCE |  |  |  | 2113.7 |
| NTI44831 |  | 35.6933289 | -81.1827774 | CARPENTER CO CONOVER | CONOVER, NC | MC | 28.9 |  |  |  |
| NTI45064 |  | 35.1497192 | -79.0022202 | FORT BRAGG MILITARY | FORT BRAGG, NC | MC,PCE,TCA | 46.3 | 18.1 | 0.1 |  |
| NTI45127 |  | 41.7834396 | -71.5176468 | MEARTHANE | CRANSTON, RI | MC | 7280.2 |  |  |  |
| NTI45263 |  | 41.8736 | -71.4100876 | PROVIDENCE METALLIZING CO., INC. | PAWTUCKET, RI | TCE |  |  |  | 6584.8 |
| NTI45366 |  | 35.6505508 | -80.4947281 | HBD INDUSTRIES INC | SALISBURY, NC | PCE |  | 499.0 |  |  |
| NTI45427 |  | 34.3202095 | -78.7394409 | FLOWLINE DIVISION | WHITEVILLE, NC | TCE |  |  |  | 8582.0 |
| NTI45456 |  | 44.9892006 | -93.2570038 | Superior Plating Inc | MINNEAPOLIS, MN | TCE |  |  |  | 1963.0 |
| NTI46048 |  | 35.7715988 | -78.5497284 | ABB AUTOMATION, INC. | RALEIGH, NC | PCE |  | 1469.6 |  |  |
| NTI46604 |  | 47.6515961 | -122.352623 | Asko Processing Inc | Seattle, WA | TCE |  |  |  | 5761.5 |
| NTI46609 |  | 47.5311012 | -122.310501 | Boeing Commercial Airplane Group (Plant 2) | Seattle, WA | TCA |  |  | 5.0 |  |
| NTI46675 |  | 47.6688538 | -122.195152 | Western Pneumatic Tube Company | Kirkland, WA | TCE |  |  |  | 18398.2 |
| NTI47980 |  | 41.7219009 | -87.6924973 | LITTLE COMPANY OF MARY HOSPITAL | EVERGREEN PARK, IL | PCE |  | 0.1 |  |  |
| NTI48022 |  | 41.9399986 | -87.8768997 | GRAPH-ON, INCORPORATED | FRANKLIN PARK, IL | TCA,TCE |  |  | 5624.5 | 5624.5 |
| NTI48035 |  | 41.9408989 | -87.8859024 | AMERICAN RIVET CO. INC. | FRANKLIN PARK, IL | TCE |  |  |  | 5533.8 |
| NTI48062 |  | 41.9506989 | -87.8884964 | SLOAN VALVE CO. | FRANKLIN PARK, IL | TCE |  |  |  | 679.5 |
| NTI48274 |  | 42.0178986 | -87.7878036 | STIMSONITE CORPORATION | NILES, IL | TCE |  |  |  | 1769.0 |
| NTI48296 |  | 42.0344009 | -87.8961029 | ADAMS ELEVATOR EQUIPMENT CO. | NILES, IL | TCE |  |  |  | 3160.6 |
| NTI48419 |  | 42.0219994 | -87.9639969 | METAL IMPACT CORP | ELK GROVE, IL | PCE |  | 3719.5 |  |  |
| NTI48445 |  | 41.9658012 | -87.8728027 | CASTLE METAL FINISHING CORPORATION | SCHILLER PARK, IL | TCE |  |  |  | 2040.7 |
| NTI48447 |  | 41.9688988 | -87.8638992 | WISCONSIN TOOL AND STAMPING CO. | SCHILLER PARK, IL | PCE,TCE |  | 7585.5 |  | 17331.8 |
| NTI48500 |  | 42.0144005 | -87.7225037 | WELCH VACUUM TECHNOLOGY | SKOKIE, IL | TCE |  |  |  | 3991.6 |
| NTI48613 |  | 41.9880981 | -88.1660995 | SENIOR FLEXONICS, INC. | BARTLETT, IL | TCE |  |  |  | 22877.1 |
| NTI48676 |  | 42.0040016 | -87.9645004 | MAGNETIC INSPECTION LAB., INC. | ELK GROVE VILLAGE, IL | PCE,TCE |  | 29029.9 |  | 11912.7 |
| NTI48732 |  | 41.9380989 | -87.6908035 | ENAMELERS AND JAPANNERS, INC.- PLANTS 1-5 | CHICAGO, IL | MC | 943.5 |  |  |  |
| NTI48889 |  | 41.9406013 | -87.6931 | HU-FRIEDY MANUFACTURING CO | CHICAGO, IL | TCE |  |  |  | 1905.1 |
| NTI48996 |  | 41.9502792 | -87.6908264 | BODINE ELECTRIC COMPANY | CHICAGO, IL | TCE |  |  |  | 2874.0 |
| NTI49452 |  | 41.8544998 | -87.6483002 | GREIF BROS. CORP., SEYMOUR AND PECK DIV. | CHICAGO, IL | TCE |  |  |  | 4666.6 |
| NTI49525 |  | 41.9287987 | -87.7315979 | GENERAL MACHINERY AND MANUFACTURING CO. | CHICAGO, IL | TCE |  |  |  | 8322.5 |
| NTI49526 |  | 41.8055992 | -87.7089005 | L AND M CAST STONE, INC. | CHICAGO, IL | TCE |  |  |  | 18869.4 |
| NTI49625 |  | 41.8524017 | -87.7369003 | ABLE ELECTROPOLISHING CO. | CHICAGO, IL | TCE |  |  |  | 14061.4 |
| NTI50167 |  | 41.7388992 | -87.9375 | MEADEN SCREW PRODUCTS COMPANY | BURR RIDGE, IL | TCE |  |  |  | 8168.7 |
| NTI51064 |  | 41.6716003 | -88.5375977 | PLANO METAL SPECIALTIES INC. | PLANO, IL | TCE |  |  |  | 5579.2 |
| NTI51145 |  | 42.3800011 | -87.9000015 | GALLAGHER CORPORATION | GURNEE, IL | TCE |  |  |  | 3628.7 |
| NTI51298 |  | 42.1567001 | -88.1369019 | BURPEE CO. | BARRINGTON, IL | TCE |  |  |  | 5691.7 |
| NTI51726 |  | 42.2447014 | -88.3199997 | JOHN CRANE INC. | CRYSTAL LAKE, IL | TCE |  |  |  | 943.5 |
| NTI51753 |  | 42.1749992 | -88.4285965 | UNION SPECIAL CORP. | HUNTLEY, IL | TCE |  |  |  | 786.9 |
| NTI51843 |  | 42.2518997 | -88.6121979 | ARNOLD ENGINEERING CO. | MARENGO, IL | PCE,TCA |  | 1950.0 | 11226.4 |  |
| NTI52191 |  | 38.6707993 | -90.177803 | SPECTRULITE CONSORTIUM INC. | MADISON, IL | TCE |  |  |  | 453.6 |
| NTI52497 |  | 42.1330986 | -89.2508011 | QUALITY METAL FINISHING CO. | BYRON, IL | TCE |  |  |  | 68414.0 |
| NTI53014 |  | 38.5928001 | -90.1752014 | CERRO COPPER PRODUCTS CO. | SAUGET, IL | TCE |  |  |  | 41276.9 |
| NTI53352 |  | 40.1436005 | -87.5963974 | DANVILLE METAL STAMPING CO. | DANVILLE, IL | PCE |  | 3527.6 |  |  |
| NTI53562 |  | 41.6273994 | -89.9537964 | STERLING MULTI PRODUCTS | PROPHETSTOWN, IL | TCE |  |  |  | 3157.5 |
| NTI53688 |  | 41.6450005 | -87.6917038 | FEDERAL SIGNAL CORP SIGNAL DIVISION | UNIVERSITY PARK, IL | TCE |  |  |  | 7028.0 |
| NTI53702 |  | 41.6506004 | -88.0547028 | CITGO PETROLEUM CORP-LEMONT REFINERY | LEMONT, IL | TCA |  |  | 6062.5 |  |
| NTI53869 |  | 42.2616997 | -89.0952988 | BARRON INDUSTRIES | ROCKFORD, IL | TCE |  |  |  | 5767.0 |
| NTI53955 |  | 42.4541702 | -89.0966721 | REED-CHATWOOD INC. | ROCKFORD, IL | TCA |  |  | 32658.6 |  |
| NTI54284 |  | 47.4925995 | -122.208801 | Boeing Commercial Airplane (Renton) | Renton, WA | MC,TCA | 9.5 |  | 69.4 |  |
| NTI54795 |  | 41.9491997 | -87.8685989 | ACRA ELECTRIC CORP. | SCHILLER PARK, IL | MC,TCE | 7183.1 |  |  | 2220.8 |
| NTI54855 |  | 42.0222015 | -87.9610977 | ACME FINISHING COMPANY | ELK GROVE VILLAGE, IL | TCE |  |  |  | 4485.6 |
| NTI54879 |  | 41.9822006 | -87.7833023 | ALERT SPRAY SERVICE CORP. | CHICAGO, IL | TCE |  |  |  | 2694.3 |
| NTI54963 |  | 41.9188995 | -87.6631012 | CLYBOURN METAL FINISHING COMPANY | CHICAGO, IL | TCE |  |  |  | 4648.4 |
| NTI55239 |  | 41.7999992 | -88.0667038 | LOCKFORMER CO. | LISLE, IL | TCE |  |  |  | 6831.1 |
| NTI55477 |  | 41.9138908 | -88.2780609 | DUKANE CORPORATION | ST. CHARLES, IL | TCE |  |  |  | 9246.0 |
| NTI55610 |  | 41.3800011 | -89.1280975 | EAKAS CORP. | PERU, IL | TCA |  |  | 77.8 |  |
| NTI55719 |  | 42.4383011 | -88.2497025 | INTERMATIC INC. | SPRING GROVE, IL | TCE |  |  |  | 25045.1 |
| NTI55774 |  | 39.8205986 | -88.9653015 | ZEXEL USA CORP. - DECATUR FACTORY | DECATUR, IL | PCE,TCA,TCE |  | 30605.1 | 16387.6 | 9979.0 |
| NTI56136 |  | 42.3008003 | -89.6149979 | MICRO SWITCH | FREEPORT, IL | TCA,TCE |  |  | 90.7 | 4517.3 |
| NTI56886 |  | 43.1788902 | -85.2405701 | NORTHLAND CORP | GREENVILLE, MI | MC | 851.7 |  |  |  |
| NTI57049 |  | 35.0611992 | -85.2742996 | SYNAIR CORPORATION | CHATTANOOGA, TN | MC | 816.5 |  |  |  |
| NTIAL0450008 |  | 31.3327999 | -85.7072983 | Fort Rucker HQ U.S. Army Aviation Center and Fort |  | PCE |  | 145.1 |  |  |
| NTIAL0950045 |  | 34.2972984 | -86.4709015 | Eaton Corporation | Arab, AL | TCA |  |  | 1451.5 |  |
| NTICA001271 |  | 37.5092049 | -121.947853 | MENLO INDUSTRIES, INC | FREMONT, CA | TCA |  |  | 6.1 |  |
| NTICA00160 |  | 37.7392807 | -122.218307 | ROLLS-ROYCE ENGINE SERVICES - | OAKLAND, CA | TCE |  |  |  | 1058.5 |
| NTICA007546 |  | 39.4986801 | -121.567238 | BLOUNT INC | OROVILLE, CA | TCA |  |  | 4943.2 |  |
| NTICA013733 |  | 37.9998016 | -121.792801 | PACIFIC GAS AND ELECTRIC COMPA | ANTIOCH, CA | TCA |  |  | 289.2 |  |
| NTICA029988 |  | 35.4200363 | -119.057793 | MOBIL CHEMICAL CO. | BAKERSFIELD, CA | TCA |  |  | 7208.0 |  |
| NTICA0371139 |  | 34.2498016 | -118.400803 | LA CO., METROPOLITAN TRANS AUT | SUN VALLEY, CA | TCA |  |  | 441.2 |  |
| NTICA0371143 |  | 34.2369156 | -118.595306 | SCHAEFFER MAGNETICS INC | CHATSWORTH, CA | TCA |  |  | 182.2 |  |
| NTICA0371152 |  | 34.0955009 | -117.747902 | LOCKHEED MARTIN ELECTRO-OPTICA | POMONA, CA | TCA |  |  | 7194.4 |  |
| NTICA0371157 |  | 34.0499001 | -118.235001 | LA CO., METROPOLITAN TRANS AUT | CHATSWORTH, CA | MC,TCA | 30.8 |  | 384.2 |  |
| NTICA0371160 |  | 33.8799019 | -118.0271 | HAYES - LEMMERZ INTERNATIONAL | LA MIRADA, CA | MC | 1897.8 |  |  |  |
| NTICA0371195 |  | 34.1498985 | -118.323196 | THE WALT DISNEY COMPANY | BURBANK, CA | TCA,TCE |  |  | 1088.1 | 81.7 |
| NTICA0371208 |  | 33.8177986 | -118.188499 | TRICO INDUSTRIES INC | SIGNAL HILL, CA | PCE,TCA |  | 59.4 | 2254.9 |  |
| NTICA0371215 |  | 33.9482498 | -118.064644 | REDI STRIP CO | SANTA FE SPRINGS, CA | MC | 1098.6 |  |  |  |
| NTICA0371221 |  | 34.2224655 | -118.493248 | KAL GARD COATING & MFG CORP | SEPULVEDA, CA | TCA |  |  | 11094.0 |  |
| NTICA0371232 |  | 34.0098991 | -118.440201 | MARCONI ASTRONICS INC | SANTA MONICA, CA | TCA |  |  | 9973.4 |  |
| NTICA0371235 |  | 34.1456413 | -118.789001 | TERADYNE INC | AGOURA HILLS, CA | TCA |  |  | 368.8 |  |
| NTICA0371243 |  | 33.8297997 | -118.329102 | M/A-COM, A DIVN. OF AMP INC. | TORRANCE, CA | TCA |  |  | 1367.2 |  |
| NTICA0371244 |  | 34.215477 | -118.594269 | CONDOR PACIFIC IND INC | CANOGA PARK, CA | MC,TCA | 1148.3 |  | 639.9 |  |
| NTICA0371263 |  | 33.9799004 | -118.0933 | NORTHROP GRUMMAN CORP, MASD | PICO RIVERA, CA | TCA |  |  | 9506.8 |  |
| NTICA0371271 |  | 33.9999008 | -118.223503 | CONSOLIDATED FABRICATORS CORP | VERNON, CA | TCA |  |  | 536.6 |  |
| NTICA0371308 |  | 34.0499001 | -118.235001 | LA CO., METROPOLITAN TRANS AUT | LOS ANGELES, CA | MC,TCA | 41.7 |  | 469.9 |  |
| NTICA0371319 |  | 34.0399017 | -118.148201 | SO CAL GAS CO | MONTEREY PARK, CA | MC,TCA | 0.4 |  | 0.4 |  |
| NTICA0371331 |  | 34.2629242 | -118.656784 | WAMBOLD FURNITURE | SIMI VALLEY, CA | TCA |  |  | 549.8 |  |
| NTICA0371347 |  | 33.9986992 | -118.3209 | LA CO., METROPOLITAN TRANS AUT | LOS ANGELES, CA | MC,TCA | 32.7 |  | 356.5 |  |
| NTICA0371359 |  | 33.9897995 | -117.898499 | PUREX POOL SYSTEMS INC | INDUSTRY, CA | TCA |  |  | 13258.0 |  |
| NTICA0371361 |  | 33.9309883 | -118.418541 | ALLIED-SIGNAL INC,GARRETT GEN | LOS ANGELES, CA | MC,TCA | 2547.0 |  | 56.2 |  |
| NTICA0371364 |  | 33.8829269 | -118.014709 | QUEEN CARPET CORP, TUFTEX CARP | LA MIRADA, CA | MC | 342.9 |  |  |  |
| NTICA0371367 |  | 34.0914001 | -118.051399 | THE VONS COMPANIES INC | EL MONTE, CA | TCA |  |  | 187.3 |  |
| NTICA0371369 |  | 33.9299011 | -118.125099 | U.S.ORDNANCE CO.,PRIMEX TECHNO | DOWNEY, CA | MC,TCA | 2235.3 |  | 1233.3 |  |
| NTICA0371372 |  | 34.1763992 | -118.312798 | ALLIEDSIGNAL AEROSPACE, W COAS | BURBANK, CA | MC,TCA | 189.2 |  | 979.1 |  |
| NTICA0371378 |  | 33.9971008 | -118.212601 | BARKSDALE INC | LOS ANGELES, CA | MC,TCA,TCE | 277.7 |  | 1417.0 | 313.0 |
| NTICA0371384 |  | 34.0397987 | -118.700699 | HRL LABORATORIES, LLC | MALIBU, CA | TCA |  |  | 12.8 |  |
| NTICA0371392 |  | 33.8596001 | -118.156601 | SULLY-MILLER CONTRACTING CO,BL | LONG BEACH, CA | PCE |  | 95.3 |  |  |
| NTICA0371477 |  | 33.8097992 | -118.3396 | CUSHION CUT INC | TORRANCE, CA | TCA |  |  | 5687.1 |  |
| NTICA0371478 |  | 34.1837006 | -118.605904 | DATA PROD. CORP | WOODLAND HILLS, CA | TCA |  |  | 147.0 |  |
| NTICA0371497 |  | 34.2999001 | -118.477699 | BEI SYSTRON DONNER CO, EDCLIFF | SYLMAR, CA | TCA |  |  | 1770.6 |  |
| NTICA0371508 |  | 34.1782188 | -118.589272 | THE BOEING COMPANY | CANOGA PARK, CA | PCE,TCA |  | 5367.2 | 118605.6 |  |
| NTICA0371525 |  | 34.0088158 | -118.234993 | BENDER MACHINE INC | LOS ANGELES, CA | TCA |  |  | 105.7 |  |
| NTICA0371529 |  | 33.8199959 | -118.258125 | HUCK INTERNATIONAL INC | CARSON, CA | TCA |  |  | 24665.9 |  |
| NTICA0371551 |  | 33.8932533 | -118.031662 | TUFTEX CARPET MILLS INC,LA MIR | SANTA FE SPRINGS, CA | MC | 342.9 |  |  |  |
| NTICA0371561 |  | 34.2282143 | -118.579239 | THE BOEING COMPANY | CANOGA PARK, CA | TCA |  |  | 28624.4 |  |
| NTICA0371587 |  | 33.919899 | -118.135803 | THE BOEING COMPANY | DOWNEY, CA | TCA |  |  | 10426.7 |  |
| NTICA0371606 |  | 33.9297981 | -118.395599 | BOEING SATELLITE SYSTEMS INC | EL SEGUNDO, CA | MC,TCA | 353.6 |  | 1714.4 |  |
| NTICA0378 |  | 34.1271095 | -117.927902 | PERKINELMER OPTOELECTRONICS SC | AZUSA, CA | MC,TCA | 12797.2 |  | 28183.5 |  |
| NTICA0379 |  | 33.8498993 | -118.329399 | HONEYWELL INTERNATIONAL INC | TORRANCE, CA | TCA |  |  | 6241.7 |  |
| NTICA0379995 |  | 34.4297981 | -118.577904 | HR TEXTRON INC. | PACOIMA, CA | TCA |  |  | 6743.6 |  |
| NTICA0379999 |  | 34.4297981 | -118.577904 | HR TEXTRON INC | VALENCIA, CA | TCA |  |  | 13252.8 |  |
| NTICA0531869 |  | 36.8055 | -121.789398 | DUKE ENERGY MOSS LANDING LLC | MOSS LANDING, CA | MC | 1397.1 |  |  |  |
| NTICA05920 |  | 33.6498985 | -117.862602 | CONEXANT SYSTEMS INC | NEWPORT BEACH, CA | TCA |  |  | 277.6 |  |
| NTICA0592016 |  | 33.7099991 | -117.841698 | TROY SYSTEMS INC | SANTA ANA, CA | TCA |  |  | 2173.8 |  |
| NTICA0592024 |  | 33.7196007 | -117.8526 | MARK OPTICS INC. | SANTA ANA, CA | TCA |  |  | 3353.0 |  |
| NTICA0592031 |  | 33.7098999 | -117.852501 | TEXTRON AEROSPACE FASTENERS | SANTA ANA, CA | TCA |  |  | 16879.9 |  |
| NTICA0592045 |  | 33.7036629 | -117.996346 | REVCO PRODUCTS INC | HUNTINGTON BEACH, CA | TCA |  |  | 136.4 |  |
| NTICA0592046 |  | 33.7056885 | -117.907951 | ROI DEVELOPMENT CORP | SANTA ANA, CA | TCA |  |  | 988.8 |  |
| NTICA0592051 |  | 33.7202339 | -117.910248 | SUPERIOR MANUFACTURING CO | SANTA ANA, CA | TCA |  |  | 2439.4 |  |
| NTICA0592053 |  | 33.7000008 | -117.852402 | 3M MEDICAL PRODUCTS | IRVINE, CA | MC,TCA | 4100.5 |  | 3224.1 |  |
| NTICA0592066 |  | 33.8587532 | -117.836433 | ROTO-INDUSTRIES, INC | ANAHEIM, CA | MC,TCA | 2582.8 |  | 171.9 |  |
| NTICA0592069 |  | 33.919899 | -117.919403 | IAC INDUSTRIES | BREA, CA | TCA |  |  | 9797.6 |  |
| NTICA0592070 |  | 33.8599014 | -117.843102 | THE BOEING COMPANY | ANAHEIM, CA | TCA |  |  | 13426.2 |  |
| NTICA0592075 |  | 33.8081322 | -118.054893 | FURON COMPANY MECHANICAL SEAL | LOS ALAMITOS, CA | TCA |  |  | 789.2 |  |
| NTICA0592076 |  | 33.7081184 | -117.849281 | EMBEE PLATING CO | SANTA ANA, CA | TCA |  |  | 21152.8 |  |
| NTICA0592131 |  | 33.7198982 | -117.831001 | RICOH ELECTRONICS INC | IRVINE, CA | MC,PCE | 8878.2 | 13518.0 |  |  |
| NTICA0592137 |  | 33.8498993 | -117.897102 | KIMBERLY-CLARK WORLDWIDE INC.- | FULLERTON, CA | TCA |  |  | 34182.3 |  |
| NTICA0652160 |  | 33.9178619 | -116.851997 | JACK STANFIELD CO INC, STANFIE | BANNING, CA | TCA |  |  | 2280.7 |  |
| NTICA0652166 |  | 33.4949112 | -117.153099 | NATL PROCESS IND, INC | TEMECULA, CA | TCA |  |  | 302.1 |  |
| NTICA0652176 |  | 33.8303909 | -117.247299 | PACIFIC WESTERN EXTRUDED PLAST | PERRIS, CA | TCA |  |  | 75.5 |  |
| NTICA0652187 |  | 33.8799019 | -117.594704 | HONEYWELL THERMAL SYSTEMS | CORONA, CA | TCA |  |  | 6383.2 |  |
| NTICA0672219 |  | 38.5107346 | -121.380852 | THE PALM IRON & BRIDGE WORKS | SACRAMENTO, CA | MC,TCA | 1769.0 |  | 1369.8 |  |
| NTICA0712392 |  | 34.8913574 | -116.878746 | US ARMY NATIONAL TRAINING CTR. | FORT IRWIN, CA | PCE,TCA |  | 6.4 | 6.4 |  |
| NTICA0712416 |  | 34.8361511 | -115.969704 | MWD - IRON MT. PUMPING STATION | DESERT CENTER, CA | TCA |  |  | 823.3 |  |
| NTICA0712418 |  | 34.262455 | -114.166298 | MWD - GENE INTAKE PUMPING PLT. | PARKER DAM, CA | TCA |  |  | 1646.5 |  |
| NTICA0712464 |  | 34.0439148 | -117.612534 | MAG INSTRUMENT INC | ONTARIO, CA | TCA |  |  | 14220.1 |  |
| NTICA0712501 |  | 34.089901 | -117.607002 | GENERAL MARBLE | GUASTI, CA | MC | 5443.1 |  |  |  |
| NTICA0713037 |  | 38.0168991 | -122.362099 | MSC PRE FINISH METALS INC | RICHMOND, CA | TCA |  |  | 437.9 |  |
| NTICA07324 |  | 32.8259583 | -117.151169 | PILKINGTON/BARNES HIND | SAN DIEGO, CA | TCA |  |  | 5334.2 |  |
| NTICA0732551 |  | 32.8819084 | -117.162041 | COMPOSITE OPTICS, INC. | SAN DIEGO, CA | TCA |  |  | 269.4 |  |
| NTICA0732595 |  | 32.8243065 | -117.156815 | SD TRANSIT CORP | SAN DIEGO, CA | MC,PCE,TCA | 0.5 | 0.9 | 0.9 |  |
| NTICA0732603 |  | 32.6300201 | -117.106262 | SOUTHBAY BOAT YARD | CHULA VISTA, CA | MC,PCE,TCA | 0.1 | 0.2 | 0.2 |  |
| NTICA0732639 |  | 32.8124084 | -117.216789 | BKM INC. | SAN DIEGO, CA | PCE,TCA |  | 0.1 | 0.1 |  |
| NTICA0732675 |  | 33.1385574 | -117.219086 | KILLION INDUSTRIES | VISTA, CA | PCE |  | 613.3 |  |  |
| NTICA0732681 |  | 32.635952 | -117.099579 | ROHR INDUSTRIES. | CHULA VISTA, CA | TCA |  |  | 4102.6 |  |
| NTICA0732740 |  | 32.6991501 | -117.203148 | USN NORTH ISLAND | SAN DIEGO, CA | MC,PCE,TCA | 9621.8 | 4.3 | 37.6 |  |
| NTICA0732742 |  | 32.6561813 | -117.10144 | PACORD INC. | NATIONAL CITY, CA | PCE,TCA |  | 0.1 | 0.1 |  |
| NTICA0732754 |  | 32.9415855 | -117.038872 | ALDILA - POWAY | POWAY, CA | MC | 1332.2 |  |  |  |
| NTICA0732901 |  | 32.8082275 | -116.966881 | STRIP SHOP THE | EL CAJON, CA | MC | 3604.9 |  |  |  |
| NTICA0732960 |  | 32.8181305 | -116.978714 | CARPENTER SPECIAL PRODUCTS | EL CAJON, CA | PCE |  | 1599.6 |  |  |
| NTICA0732967 |  | 33.2133293 | -117.39444 | OCEANSIDE MARINE CENTRE, INC. | OCEANSIDE, CA | MC,PCE,TCA | 0.0 | 0.0 | 0.0 |  |
| NTICA0732968 |  | 32.6953545 | -117.138649 | NORTH STAR PROPELLER, INC. | SAN DIEGO, CA | MC,PCE,TCA | 0.1 | 0.1 | 0.1 |  |
| NTICA0732973 |  | 33.1023941 | -117.218056 | HUNTER INDUSTRIES | SAN MARCOS, CA | MC,PCE,TCA,TCE | 13.9 | 2.1 | 23.4 | 59.1 |
| NTICA0732977 |  | 33.2127342 | -117.264038 | BRILES RIVET CORP | OCEANSIDE, CA | TCA |  |  | 1290.5 |  |
| NTICA0732981 |  | 32.8261795 | -116.986687 | BUCK KNIVES, INC | EL CAJON, CA | PCE |  | 1216.9 |  |  |
| NTICA0732984 |  | 33.1484299 | -117.216232 | KILLION INDUSTRIES | VISTA, CA | PCE |  | 153.3 |  |  |
| NTICA0732990 |  | 32.8270607 | -117.12339 | MAXWELL LABORATORIES | SAN DIEGO, CA | TCA |  |  | 2179.6 |  |
| NTICA0733011 |  | 32.6905746 | -117.120468 | PACIFIC SHIP REPAIR & FABRICAT | SAN DIEGO, CA | PCE,TCA |  | 0.4 | 0.2 |  |
| NTICA0733188 |  | 32.598278 | -117.081207 | MARINE SERVICE COMMERCIAL DIVI | CHULA VISTA, CA | MC,PCE,TCA | 0.0 | 0.0 | 0.0 |  |
| NTICA0733201 |  | 32.8815842 | -117.132256 | USMC AIR STATION/MIRAMAR | SAN DIEGO, CA | MC,PCE,TCA | 3.2 | 5.3 | 5.3 |  |
| NTICA0733205 |  | 32.6806717 | -117.123932 | USN 32ND ST NAV STATION | SAN DIEGO, CA | MC,PCE,TCA | 3.1 | 5.2 | 5.2 |  |
| NTICA0733211 |  | 32.7241096 | -117.21534 | USN AMPHIBIOUS BASE | CORONADO, CA | PCE |  | 1.2 |  |  |
| NTICA0733419 |  | 32.5790749 | -117.11657 | USN SUBMARINE BASE | SAN DIEGO, CA | MC,PCE,TCA | 0.3 | 0.6 | 0.6 |  |
| NTICA0733422 |  | 32.8535118 | -116.969933 | RCP BLOCK & BRICK | SANTEE, CA | MC,PCE,TCA | 0.0 | 0.0 | 0.0 |  |
| NTICA0733441 |  | 32.772747 | -117.071297 | S. D. STATE UNIVERSITY | SAN DIEGO, CA | MC,PCE | 4.5 | 10.9 |  |  |
| NTICA0753671 |  | 37.7556992 | -122.387001 | SOUTHERN ENERGY CALIFORNIA, PO | SAN FRANCISCO, CA | TCA |  |  | 91.0 |  |
| NTICA0753673 |  | 37.7366982 | -122.387199 | PG & E CO, HUNTERS POINT POWER | SAN FRANCISCO, CA | TCA |  |  | 24.7 |  |
| NTICA0773887 |  | 37.7212677 | -121.481033 | Tracy Operators | Tracy, CA | PCE |  | 0.1 |  |  |
| NTICA0773905 |  | 37.9180717 | -121.26049 | BP CHEMICALS INC | STOCKTON, CA | TCA |  |  | 1278.7 |  |
| NTICA0814053 |  | 37.4823837 | -122.173241 | ECI PAINTING, INC | MENLO PARK, CA | TCA |  |  | 1602.5 |  |
| NTICA0834297 |  | 34.4314995 | -119.873001 | Raytheon Systems Company- Buil |  | MC,PCE,TCA | 32.5 | 198.4 | 310.8 |  |
| NTICA0834308 |  | 34.4320068 | -119.866852 | Raytheon-Bldgs B1,2,3, & 6 (In | Goleta, CA | MC,TCA,TCE | 17.1 |  | 1613.1 | 5.4 |
| NTICA0834311 |  | 34.4241982 | -119.592949 | JOSTENS, INC. | SUMMERLAND, CA | TCA |  |  | 0.8 |  |
| NTICA0834333 |  | 34.4301643 | -119.861221 | JOSLYN ELECTRONIC SYSTEMS CORP | GOLETA, CA | TCA |  |  | 2559.6 |  |
| NTICA0854523 |  | 37.4053154 | -122.027664 | LOCKHEED MARTIN CORPORATION | SUNNYVALE, CA | TCA |  |  | 2.2 |  |
| NTICA0854524 |  | 37.3950424 | -122.050247 | E/M, A DIVISION OF MORGAN CHEM | MOUNTAIN VIEW, CA | TCA |  |  | 1036.4 |  |
| NTICA0854535 |  | 37.4031754 | -121.882034 | QUICK SIL INC | SAN JOSE, CA | TCA |  |  | 0.2 |  |
| NTICA0854614 |  | 37.4511986 | -122.129501 | SARONIX | PALO ALTO, CA | TCA |  |  | 167.3 |  |
| NTICA0854622 |  | 37.4240074 | -121.88974 | LITE-ON, INC | MILPITAS, CA | TCA |  |  | 54.7 |  |
| NTICA0854625 |  | 37.3824577 | -121.969406 | INTEL CORPORATION | SANTA CLARA, CA | TCA |  |  | 3.5 |  |
| NTICA0854626 |  | 37.3834381 | -121.952049 | INTEVAC INDUSTRIES, INC | SANTA CLARA, CA | TCA |  |  | 5696.5 |  |
| NTICA0854685 |  | 37.4179993 | -122.152496 | VARIAN ONCOLOGY SYSTEMS | PALO ALTO, CA | TCA,TCE |  |  | 60.4 | 22.1 |
| NTICA0854704 |  | 37.4303017 | -122.107201 | SPACE SYSTEMS/LORAL (BLDG #25) | PALO ALTO, CA | TCA |  |  | 34.7 |  |
| NTICA0854705 |  | 37.4267006 | -122.107201 | SPACE SYSTEMS/LORAL | PALO ALTO, CA | TCA |  |  | 631.0 |  |
| NTICA0854761 |  | 37.4099007 | -122.152603 | LOCKHEED MARTIN CORPORATION, M | PALO ALTO, CA | TCA |  |  | 13.3 |  |
| NTICA0854764 |  | 37.4147797 | -121.948524 | SDL,INCORPORATED | SAN JOSE, CA | TCA |  |  | 60.7 |  |
| NTICA0854766 |  | 37.4071999 | -122.152603 | LOCKHEED MARTIN CORPORATION, M | PALO ALTO, CA | TCA |  |  | 39.9 |  |
| NTICA0854805 |  | 37.3746986 | -121.927101 | PIERCEY TOYOTA, INC | SAN JOSE, CA | MC | 55.2 |  |  |  |
| NTICA0854846 |  | 37.3871994 | -121.915703 | SANMINA CORPORATION | SAN JOSE, CA | MC | 362.5 |  |  |  |
| NTICA0854849 |  | 37.3868523 | -122.039368 | EG & G HOLDINGS, INC | SUNNYVALE, CA | TCA |  |  | 36.4 |  |
| NTICA0854883 |  | 37.4103012 | -122.084801 | TELEDYNE ELECTRONIC TECHNOLOGI | MOUNTAIN VIEW, CA | TCA |  |  | 735.0 |  |
| NTICA0854911 |  | 37.3920364 | -121.930824 | INTERNATIONAL MICROELECTRONICS | SAN JOSE, CA | TCA |  |  | 3.8 |  |
| NTICA0854914 |  | 37.3340988 | -121.916397 | PACIFIC GAS AND ELECTRIC COMPA | SAN JOSE, CA | TCA |  |  | 34.6 |  |
| NTICA0955098 |  | 38.2725754 | -121.985359 | R & M ENERGY SYSTEMS | FAIRFIELD, CA | TCA,TCE |  |  | 10055.1 | 1508.3 |
| NTICA0995303 |  | 37.6335411 | -120.95034 | TRI VALLEY GROWERS CONTAINER D | MODESTO, CA | TCA |  |  | 96.4 |  |
| NTICA1014302 |  | 36.5115967 | -119.548386 | SILGAN CONTAINERS MANUFAC CORP | KINGSBURG, CA | MC,PCE,TCA | 0.7 | 0.7 | 0.7 |  |
| NTICA10538 |  | 35.1171989 | -118.533401 | CALIFORNIA CORRECTIONAL INST |  | TCA |  |  | 1.8 |  |
| NTICA10782 |  | 34.3141632 | -117.271805 | MORENO VALLEY SCH DIST | SUNNYMEAD, CA | TCA |  |  | 0.2 |  |
| NTICA1115531 |  | 34.110199 | -119.113998 | NAVAL AIR WEAPONS STATION | POINT MUGU, CA | MC,TCA | 76.6 |  | 0.3 |  |
| NTICA1115591 |  | 34.1889 | -118.931503 | TELEDYNE ELECTRONICS | NEWBURY PARK, CA | TCA |  |  | 1509.6 |  |
| NTICA1115634 |  | 34.2326012 | -119.019402 | OPTIMUM OPTICAL SYSTEMS INC | CAMARILLO, CA | TCA |  |  | 431.3 |  |
| NTICA1115644 |  | 34.1894989 | -119.170303 | FREIGHT CONTAINER CORP. | OXNARD, CA | MC | 50.5 |  |  |  |
| NTICA1115684 |  | 34.2162018 | -119.0298 | EVEREST & JENNINGS INC | CAMARILLO CA, CA | TCA |  |  | 2370.0 |  |
| NTICA1115685 |  | 34.2060127 | -119.03157 | AIR COOLING TECHNOLOGY | CAMARILLO, CA | TCA |  |  | 2742.0 |  |
| NTICA1115692 |  | 34.2713013 | -118.726997 | ENDERLE FUEL INJECTION | SIMI VALLEY, CA | PCE,TCA |  | 3.3 | 178.8 |  |
| NTICA1115697 |  | 34.2784996 | -118.911797 | TENCAL INC. | SIMI VALLEY, CA | PCE,TCA |  | 0.1 | 0.1 |  |
| NTICA1115704 |  | 34.2234001 | -119.029999 | TRANSCO PRODUCTS INC. | CAMARILLO, CA | TCA |  |  | 1097.7 |  |
| NTICA1115736 |  | 34.257 | -119.226303 | SANTA BARBARA APPLIED OPTICS | VENTURA, CA | TCA |  |  | 678.6 |  |
| NTICA1505123 |  | 35.622467 | -117.681305 | NAVAL AIR WEAPONS STATION | CHINA LAKE, CA | MC,TCA,TCE | 0.9 |  | 1.7 | 2.7 |
| NTICA1905024 |  | 34.646801 | -118.069199 | NORTHROP GRUMMAN, SITE 4 | PALMDALE, CA | TCA |  |  | 92.6 |  |
| NTICA3116233 |  | 38.7795982 | -121.3078 | NEC ELECTRONICS INC | ROSEVILLE, CA | TCA |  |  | 1059.7 |  |
| NTICAT$12604 |  | 33.919899 | -118.384598 | NORTHROP GRUMMAN CORP, AIRCRAF | EL SEGUNDO, CA | MC,PCE,TCA | 9926.4 | 32.7 | 47383.2 |  |
| NTICO0048 |  | 38.2369995 | -104.612701 | CF&I STEEL L P DBA ROCKY MTN STEEL MILLS | PUEBLO, CO | PCE |  | 37.2 |  |  |
| NTICO0050996 |  | 39.6217995 | -104.987198 | BURT CHEVROLET | ENGLEWOOD, CO | MC | 51.8 |  |  |  |
| NTICO0130615 |  | 40.0704002 | -105.204399 | VAPOR TECHNOLOGIES INC | BOULDER, CO | TCE |  |  |  | 816.5 |
| NTICO0310511 |  | 39.7092018 | -104.9907 | TOOLS FOR BENDING INC | DENVER, CO | PCE |  | 503.3 |  |  |
| NTICO0632 |  | 40.1506996 | -105.021103 | PCC COMPOSITES | LONGMONT, CO | TCE |  |  |  | 453.6 |
| NTICO1819 |  | 39.838501 | -104.666313 | LEARJET, INC. - DIA | DENVER, CO | TCE |  |  |  | 359.9 |
| NTICTT$579 |  | 41.4583321 | -72.6833344 | DURHAM MFG. CO. | DURHAM, CT | TCE |  |  |  | 29498.5 |
| NTICTT$610 |  | 41.4541664 | -72.8291702 | CT ACQUISITIONS L.L.C. DBA DANVER | WALLINGFORD, CT | PCE |  | 36759.1 |  |  |
| NTIFL0090132 |  | 28.0510998 | -80.6062012 | DRS OPTRONICS | PALM BAY, FL | MC | 898.1 |  |  |  |
| NTIFL0250827 |  | 25.9267998 | -80.2562027 | B F GOODRICH | MIAMI, FL | TCE |  |  |  | 18787.8 |
| NTIFL0571103 |  | 27.9486008 | -82.4580994 | PHOTOENGRAVING INC | TAMPA, FL | TCE |  |  |  | 607.8 |
| NTIFL0610023 |  | 27.6548004 | -80.4160995 | THE NEW PIPER AIRCRAFT, INC | VERO BEACH, FL | MC | 7892.5 |  |  |  |
| NTIFL1010335 |  | 28.2744999 | -82.6392975 | PALL AEROPOWER CORP | NEW PORT RICHEY, FL | TCE |  |  |  | 1161.2 |
| NTIFL1030098 |  | 27.8155994 | -82.7511978 | ESSILOR OF AMERICA, INC. | ST PETERSBURG, FL | MC | 1032.8 |  |  |  |
| NTIFL1030416 |  | 27.8696995 | -82.7173996 | FLORIDA METAL STAMPING INC | LARGO, FL | TCE |  |  |  | 7135.0 |
| NTIFLR023003 |  | 30.1748104 | -82.5754013 | TIMCO | LAKE CITY, FL | MC,TCA | 72.6 |  | 9.1 |  |
| NTIFLR083013 |  | 29.2180405 | -82.1430893 | W F MICKEY BODY COMPANY | OCALA, FL | MC | 9.1 |  |  |  |
| NTIIL0075859 |  | 42.2509995 | -88.8759995 | M AND R RUBBER CO. | BELVIDERE, IL | PCE |  | 241.7 |  |  |
| NTIIL011100A |  | 41.3372002 | -89.2192001 | RONKEN INDUSTRIES, INC. | SPRING VALLEY, IL | TCE |  |  |  | 4340.9 |
| NTIIL0115886 |  | 41.3875008 | -89.4571991 | HARPER WYMAN CO | PRINCETON, IL | TCE |  |  |  | 3483.6 |
| NTIIL0115889 |  | 41.3302994 | -89.2121964 | HOBBS CORP. | SPRING VALLEY, IL | TCA |  |  | 7925.2 |  |
| NTIIL0195954 |  | 40.2779999 | -88.3840027 | BOWSHER CORPORATION | FISHER, IL | TCE |  |  |  | 1886.9 |
| NTIIL031195A |  | 42.0264015 | -87.7874985 | JOHN CRANE, INC. | MORTON GROVE, IL | TCE |  |  |  | 14582.5 |
| NTIIL03142 |  | 42.019001 | -87.7929993 | OAKLEY INDUSTRIES, INC. | NILES, IL | TCE |  |  |  | 6112.2 |
| NTIIL0316063 |  | 41.7967987 | -87.8610001 | HOLLYMATIC CORP | COUNTRYSIDE, IL | PCE |  | 3962.6 |  |  |
| NTIIL0316072 |  | 42.0206985 | -87.9129028 | MIDWEST/GENDEX DENTAL-DIV OF DENTSPLY INT'L | DES PLAINES, IL | TCA |  |  | 2721.6 |  |
| NTIIL0316147 |  | 41.9411011 | -87.8563995 | BRUNNER AND LAY INC. | FRANKLIN PARK, IL | PCE |  | 147.4 |  |  |
| NTIIL0316332 |  | 41.8549995 | -87.8575974 | ECS CORP. | BROADVIEW, IL | TCE |  |  |  | 7547.8 |
| NTIIL0316389 |  | 41.8699989 | -87.8638992 | H.A. FRAMBURG AND COMPANY | BELLWOOD, IL | TCE |  |  |  | 14285.9 |
| NTIIL0316435 |  | 42.0110016 | -87.7210007 | R. F. MAU CO. | LINCOLNWOOD, IL | MC | 8164.7 |  |  |  |
| NTIIL0316449 |  | 41.8051987 | -87.8570023 | S A HEALY CO | MC COOK, IL | TCE |  |  |  | 54.4 |
| NTIIL0316467 |  | 42.0396996 | -87.793602 | DIEBEL MANUFACTURING CO. | MORTON GROVE, IL | TCE |  |  |  | 7976.4 |
| NTIIL0316485 |  | 41.9101982 | -87.8880997 | SCHILKE MUSIC PRODUCTS | MELROSE PARK, IL | PCE,TCE |  | 651.0 |  | 943.5 |
| NTIIL0316542 |  | 41.8193016 | -87.862999 | MUSSER DIVISION-SELMER COMPANY, INC. | LA GRANGE, IL | MC | 2090.2 |  |  |  |
| NTIIL0316594 |  | 41.9496994 | -87.8636017 | CELCO INDUSTRIES, INC. | SCHILLER PARK, IL | TCA,TCE |  |  | 19548.7 | 14723.6 |
| NTIIL0316611 |  | 41.975399 | -87.8666 | TWR SERVICE CORP | ROSEMONT, IL | TCE |  |  |  | 2830.4 |
| NTIIL0316627 |  | 42.0605011 | -88.0572891 | ECM MOTOR COMPANY | SCHAUMBURG, IL | TCA |  |  | 3962.6 |  |
| NTIIL0316639 |  | 42.026001 | -87.7149963 | RAULAND-BORG CORP. | SKOKIE, IL | TCE |  |  |  | 3628.7 |
| NTIIL0316641 |  | 42.0187988 | -87.7189026 | OHMITE MANUFACTURING CO. | SKOKIE, IL | TCE |  |  |  | 3445.0 |
| NTIIL0316669 |  | 42.0141983 | -87.7202988 | ROGERS METAL PROCESSING | SKOKIE, IL | PCE |  | 6483.8 |  |  |
| NTIIL0316674 |  | 42.0270004 | -87.7220001 | CASTING IMPREGNATORS INC. | SKOKIE, IL | TCE |  |  |  | 1504.8 |
| NTIIL0316678 |  | 42.1481018 | -87.8688965 | NATIONAL COATING TECH. | NORTHBROOK, IL | TCA |  |  | 1332.5 |  |
| NTIIL0316686 |  | 42.1455994 | -87.8531036 | RAMCEL ENGINEERING CO. | NORTHBROOK, IL | MC | 6531.7 |  |  |  |
| NTIIL0316702 |  | 42.0189018 | -87.785202 | SYNCHRO-START PRODUCTS INC. | NILES, IL | MC | 471.7 |  |  |  |
| NTIIL0316720 |  | 42.019001 | -87.7809982 | DRAWN METAL PRODUCTS DIVISION | NILES, IL | TCE |  |  |  | 1741.8 |
| NTIIL0316721 |  | 42.0159988 | -87.7819977 | SATE-LITE MANUFACTURING CO. | NILES, IL | TCE |  |  |  | 707.6 |
| NTIIL0316723 |  | 41.9216499 | -88.3041763 | A.B. DICK CO. | NILES, IL | PCE |  | 2712.5 |  |  |
| NTIIL0316747 |  | 41.9249001 | -87.8388977 | FORT LOCK CORP | RIVER GROVE, IL | TCE |  |  |  | 181.4 |
| NTIIL0316811 |  | 41.5727997 | -87.6132965 | DRUM PARTS MIDWEST CO. | THORNTON, IL | TCE |  |  |  | 1132.2 |
| NTIIL0316822 |  | 42.1272011 | -87.9206009 | REXNORD SEAL DIVISION | WHEELING, IL | TCE |  |  |  | 1272.2 |
| NTIIL0316841 |  | 42.0295982 | -87.9801025 | NORTON PERFORMANCE PLASTICS CORP | ELK GROVE, IL | TCE |  |  |  | 943.5 |
| NTIIL0316842 |  | 42.0031013 | -88.0074997 | LIGHTNING METAL SPECIALTY | ELK GROVE VILLAGE, IL | TCE |  |  |  | 21625.9 |
| NTIIL0316873 |  | 41.8993988 | -87.8992004 | HI TEMP INC | NORTHLAKE, IL | TCE |  |  |  | 12736.9 |
| NTIIL0316967 |  | 41.9350014 | -87.6932983 | CHICAGO MODERN PLATING CO | CHICAGO, IL | TCE |  |  |  | 3773.9 |
| NTIIL0316985 |  | 41.9458008 | -87.7164001 | RAULAND-BORG CORPORATION | CHICAGO, IL | TCE |  |  |  | 91.4 |
| NTIIL0316995 |  | 41.8838997 | -87.6493988 | CHICAGO-ALLIS MFG. CORP. | CHICAGO, IL | PCE |  | 2.3 |  |  |
| NTIIL0317020 |  | 41.8072014 | -87.6992035 | CENTRAL DIE CASTING | CHICAGO, IL | PCE |  | 7925.2 |  |  |
| NTIIL0317093 |  | 41.8156013 | -87.7139969 | YALE POLISHING AND PLATING | CHICAGO, IL | TCA |  |  | 825.5 |  |
| NTIIL0317139 |  | 41.8877983 | -87.6672974 | NOBERT PLATING CO | CHICAGO, IL | TCE |  |  |  | 1943.8 |
| NTIIL0317140 |  | 41.8802986 | -87.6575012 | BARNES PLATING CORP | CHICAGO, IL | TCE |  |  |  | 320.8 |
| NTIIL0317197 |  | 41.9296989 | -87.6753006 | PLASTICS CAPACITORS INC PLANT 2 | CHICAGO, IL | TCE |  |  |  | 2000.3 |
| NTIIL0317202 |  | 41.9594002 | -87.6744003 | BOYE NEEDLE, DIV. OF WM. E. WRIGHT | CHICAGO, IL | TCE |  |  |  | 48.5 |
| NTIIL0317290 |  | 41.9366989 | -87.685997 | CHICAGO CUTTING DIE CO. | CHICAGO, IL | TCE |  |  |  | 2612.7 |
| NTIIL0317360 |  | 41.885601 | -87.6675034 | IMPERIAL JAPPANING CO. | CHICAGO, IL | TCE |  |  |  | 7076.0 |
| NTIIL0317512 |  | 41.8250008 | -87.6690979 | ADVANCE METAL FINISHING COMPANY | CHICAGO, IL | PCE |  | 3628.7 |  |  |
| NTIIL0317662 |  | 41.9150009 | -87.7389984 | MILTON INDUSTRIES INC. | CHICAGO, IL | TCE |  |  |  | 907.2 |
| NTIIL0317669 |  | 41.9389992 | -87.6880035 | BULAW WELDING | CHICAGO, IL | TCE |  |  |  | 3453.1 |
| NTIIL0317672 |  | 41.8207016 | -87.6501999 | BEECO TECHNOLOGY | CHICAGO, IL | TCA |  |  | 16655.9 |  |
| NTIIL0317689 |  | 41.9813995 | -87.760498 | R S OWENS AND COMPANY | CHICAGO, IL | TCE |  |  |  | 6123.5 |
| NTIIL0317835 |  | 41.9538994 | -87.8702011 | KARR TOOL AND ENGINEERING CO. | SCHILLER PARK, IL | PCE |  | 1886.9 |  |  |
| NTIIL043020A |  | 41.9049988 | -88.1019974 | METALS TECHNOLOGY CORP. | CAROL STREAM, IL | TCE |  |  |  | 20697.0 |
| NTIIL043095A |  | 41.7999992 | -87.9666977 | AMERICAN COUPLINGS CO. | WESTMONT, IL | TCE |  |  |  | 5987.4 |
| NTIIL0437946 |  | 41.9250984 | -88.0851974 | DUPAGE MACHINE | GLENDALE HEIGHTS, IL | MC | 2494.8 |  |  |  |
| NTIIL0437960 |  | 41.8075981 | -88.0485992 | LUCENT TECHNOLOGIES INC. | LISLE, IL | TCE |  |  |  | 14505.9 |
| NTIIL0437995 |  | 41.9099998 | -87.973999 | KEPNER PRODUCTS CO. | VILLA PARK, IL | TCE |  |  |  | 1020.6 |
| NTIIL0438058 |  | 41.7999992 | -88.0417023 | TRICON IND | DOWNERS GROVE, IL | PCE |  | 943.5 |  |  |
| NTIIL0438061 |  | 41.8953018 | -88.1228027 | GERLIN, INC. | CAROL STREAM, IL | TCE |  |  |  | 5443.1 |
| NTIIL0438066 |  | 41.7743988 | -88.0421982 | FLEXIBLE STEEL LACING CO. | DOWNERS GROVE, IL | TCE |  |  |  | 1814.4 |
| NTIIL0438067 |  | 41.9049988 | -88.0994034 | MAGNETROL INTERNATIONAL | DOWNERS GROVE, IL | TCE |  |  |  | 4535.9 |
| NTIIL0438068 |  | 41.7928009 | -88.0374985 | REXNORD CORP.- REX BEARING DIV. | DOWNERS GROVE, IL | TCE |  |  |  | 3628.7 |
| NTIIL0438073 |  | 41.7916985 | -88.0417023 | TRICON INDUSTRIES INC. | DOWNERS GROVE, IL | PCE |  | 804.3 |  |  |
| NTIIL0438080 |  | 41.9770012 | -87.9869995 | DE AMERTEK CORPORATION, INC. | OAK BROOK, IL | TCE |  |  |  | 84.9 |
| NTIIL0438118 |  | 41.9710999 | -87.9424973 | L.D. REDMER SCREW PRODUCTS INC. | BENSENVILLE, IL | TCE |  |  |  | 3175.1 |
| NTIIL0458147 |  | 39.5988998 | -87.6936035 | MECO INC | PARIS, IL | PCE |  | 6595.7 |  |  |
| NTIIL0638273 |  | 41.3833008 | -88.4167023 | BIMET CORPORATION | MORRIS, IL | PCE |  | 1311.8 |  |  |
| NTIIL0738305 |  | 41.4042015 | -90.1639023 | SPRINGFIELD, INC. | GENESEO, IL | TCA |  |  | 1564.9 |  |
| NTIIL089080A |  | 41.9959984 | -88.2929993 | HEAD INC. | SOUTH ELGIN, IL | TCE |  |  |  | 8164.7 |
| NTIIL0898406 |  | 41.7561989 | -88.4404984 | OAK GRIGSBY, INC. | SUGAR GROVE, IL | MC | 317.5 |  |  |  |
| NTIIL0898477 |  | 42.0730019 | -88.2959976 | WAUCONDA TOOL AND ENGINEERING CO INC | ELGIN, IL | TCE |  |  |  | 1882.2 |
| NTIIL0898484 |  | 41.9229012 | -88.3021011 | MET-CO INDUSTRIES | ST. CHARLES, IL | TCA |  |  | 1527.2 |  |
| NTIIL0898512 |  | 42.0685005 | -88.3115005 | AMERICAN NTN BEARING MFG CORP - ELGIN PLANT | ELGIN, IL | TCA |  |  | 7850.5 |  |
| NTIIL0978631 |  | 42.1927986 | -88.1166992 | C.M. PRODUCTS, INC. | LAKE ZURICH, IL | TCE |  |  |  | 5715.3 |
| NTIIL0978698 |  | 42.3638992 | -87.8332977 | NOSCO INC. | WAUKEGAN, IL | PCE |  | 1469.0 |  |  |
| NTIIL0978727 |  | 42.2589989 | -87.9869995 | WISCONSIN TOOL AND STAMPING CO. | MUNDELEIN, IL | TCE |  |  |  | 3401.9 |
| NTIIL0998825 |  | 41.1268997 | -88.7981033 | TELEWELD, INC. | STREATOR, IL | TCE |  |  |  | 2540.1 |
| NTIIL111005A |  | 42.1702995 | -88.2988968 | WAUCONDA TOOL AND ENGINEERING | ALGONQUIN, IL | TCE |  |  |  | 3608.8 |
| NTIIL1118956 |  | 42.4805984 | -88.3091965 | CLAUD S. GORDON COMPANY | RICHMOND, IL | TCE |  |  |  | 2367.8 |
| NTIIL1118985 |  | 42.2013016 | -88.2360992 | DUREX INTERNATIONAL CORPORATION | CARY, IL | PCE |  | 1348.0 |  |  |
| NTIIL1118996 |  | 42.2481995 | -88.3104019 | PRECISION TWIST DRILL CO. | CRYSTAL LAKE, IL | MC | 3962.6 |  |  |  |
| NTIIL1118997 |  | 42.2029991 | -88.3509979 | PRECISION TWIST DRILL | CRYSTAL LAKE, IL | PCE |  | 44.2 |  |  |
| NTIIL1118998 |  | 42.2446022 | -88.307579 | AUTOTROL CORP. | CRYSTAL LAKE, IL | TCE |  |  |  | 1611.2 |
| NTIIL1119000 |  | 42.2083015 | -88.2574997 | ELECPAC DIV | CARY, IL | TCA |  |  | 849.1 |  |
| NTIIL1119043 |  | 42.2378006 | -88.3150024 | G AND M MFG CORP | CRYSTAL LAKE, IL | MC | 8304.8 |  |  |  |
| NTIIL1419397 |  | 41.9166985 | -89.0541992 | EATON CORPORATION CONTROLS DIVISION | ROCHELLE, IL | TCE |  |  |  | 3628.7 |
| NTIIL1439428 |  | 40.6986008 | -89.5727997 | HAWKEYE RUBBER MFG. CO. | PEORIA, IL | TCA |  |  | 943.5 |  |
| NTIIL167005A |  | 39.7994003 | -89.6474991 | DICKEY-JOHN CORPORATION | AUBURN, IL | TCE |  |  |  | 5613.2 |
| NTIIL18396 |  | 40.1395988 | -87.5864029 | VERMILION RUBBER TECHNOLOGY, INC. | DANVILLE, IL | TCE |  |  |  | 10793.7 |
| NTIIL1839883 |  | 40.1267014 | -87.6453018 | THERMO TECHNIQUES | DANVILLE, IL | TCE |  |  |  | 5443.1 |
| NTIIL1839900 |  | 40.1274986 | -87.6442032 | DANVILLE METAL STAMPING CO. INC. | DANVILLE, IL | PCE |  | 5112.4 |  |  |
| NTIIL1919950 |  | 38.3767014 | -88.365799 | AIRTEX PRODUCTS INC | FAIRFIELD, IL | TCA |  |  | 682.2 |  |
| NTIIL201109 |  | 42.2374992 | -89.0543976 | HAMILTON SUNDSTRAND | ROCKFORD, IL | TCA |  |  | 12047.4 |  |
| NTIIL201810A |  | 42.4543991 | -89.018898 | ECOLAB INC | SOUTH BELOIT, IL | TCA |  |  | 15.9 |  |
| NTIIL227 |  | 42.4482994 | -89.0591965 | WOODWARD GOVERNOR CO. | ROCKTON, IL | MC | 148.6 |  |  |  |
| NTIIL241 |  | 42.2000999 | -89.0570984 | CHEMICAL PROCESSING INC. | ROCKFORD, IL | TCE |  |  |  | 5943.9 |
| NTIIL292 |  | 42.2400017 | -89.0738983 | HAMILTON SUNDSTRAND | ROCKFORD, IL | PCE |  | 1088.6 |  |  |
| NTIIL323 |  | 42.4561005 | -89.0394974 | REGAL-BELOIT CORP | SOUTH BELOIT, IL | TCA |  |  | 1386.9 |  |
| NTIIL91 |  | 41.4427986 | -88.2022018 | METALSTAMP INC | CHANNAHON, IL | TCA |  |  | 1973.1 |  |
| NTIIN00247 |  | 41.6338463 | -87.5109634 | VERMETTE MACHINE CO., INC. | HAMMOND, IN | TCE |  |  |  | 2721.6 |
| NTIIN0390015 |  | 41.6921005 | -85.9943008 | E.K. BLESSING COMPANY, INC. | ELKHART, IN | TCE |  |  |  | 16025.9 |
| NTIKS00075 |  | 37.6511116 | -97.4088898 | CESSNA AIRCRAFT CO.-PAWNEE FACILITY | WICHITA, KS | MC,TCE | 3819.2 |  |  | 18143.7 |
| NTIKS00165 |  | 37.6672363 | -97.3760757 | GLOBE ENGINEERING | WICHITA, KS | TCE |  |  |  | 7257.5 |
| NTIKY1131 |  | 36.9701004 | -86.4765015 | DETREX PARTS CLEANING SER | BOWLING GREEN, KY | TCE |  |  |  | 58468.0 |
| NTIKY1141 |  | 38.0578995 | -84.7261963 | TEXAS INSTRUMENTS | VERSAILLES, KY | TCE |  |  |  | 598.7 |
| NTIKY1145 |  | 38.0649986 | -84.7225037 | YH AMERICA INCORPORATED | VERSAILLES, KY | PCE,TCA |  | 91.4 | 3666.7 |  |
| NTIKY209249 |  | 38.1986008 | -84.5516968 | PIONEER PLATING LLC | GEORGETOWN, KY | TCA |  |  | 37194.6 |  |
| NTIKY719 |  | 38.0615997 | -84.927803 | GENERAL CABLE COMPANY | LAWRENCEBURG, KY | TCE |  |  |  | 13281.2 |
| NTIKY793 |  | 37.9872017 | -84.1704025 | COSMO WHEELS INC | WINCHESTER, KY | TCA |  |  | 272.2 |  |
| NTIKY804 |  | 37.7671013 | -87.118103 | MPD, INC | OWENSBORO, KY | TCE |  |  |  | 796.9 |
| NTIKY829 |  | 38.0435982 | -84.4701996 | CENTRAL KY PROCESS | LEXINGTON, KY | TCE |  |  |  | 5443.1 |
| NTIKY909 |  | 37.8078003 | -87.6407013 | GIBBS DIE CASTING ALUMIN | HENDERSON, KY | TCA |  |  | 13374.5 |  |
| NTIKY917 |  | 37.8041992 | -87.6371994 | GIBBS DIE CASTING ALUMINM | HENDERSON, KY | TCA |  |  | 3.9 |  |
| NTIKY987 |  | 36.8521996 | -86.9092026 | J S TECHNOS CORPORATION | RUSSELLVILLE, KY | TCE |  |  |  | 7528.0 |
| NTILA1150010 |  | 31.0485592 | -93.208519 | JRTC & FT POLK/FT POLK | FT. POLK, LA | MC,PCE,TCA | 16.8 | 1.4 | 1.4 |  |
| NTIMI14370 |  | 42.6831017 | -83.1176987 | PARKEDALE PHARMACEUTICALS, INC. | ROCHESTER, MI | TCA |  |  | 197.8 |  |
| NTIMI2612119 |  | 43.2340393 | -86.187912 | GENERAL DYNAMICS LAND SYSTEMS MUSKEGON | MUSKEGON, MI | TCA |  |  | 308.4 |  |
| NTIMIA0155 |  | 42.6397285 | -85.3168335 | HASTINGS FIBERGLASS PRODUCTS INC | HASTINGS, MI | MC | 24.9 |  |  |  |
| NTIMIA2416 |  | 42.8861313 | -85.5550537 | STEPHENSON AND LAWYER INC | GRAND RAPIDS, MI | MC | 3735.3 |  |  |  |
| NTIMIA2447 |  | 42.9056206 | -85.6770935 | INTERNAL GRINDING ABRASIVE | GRAND RAPIDS, MI | MC,PCE | 10.0 | 1007.0 |  |  |
| NTIMIA2677 |  | 42.9330482 | -85.7132568 | AMERIKAM | GRAND RAPIDS, MI | TCE |  |  |  | 3054.0 |
| NTIMIA2931 |  | 42.5963593 | -83.9374084 | DIAMOND CHROME PLATING INC | HOWELL, MI | TCE |  |  |  | 7194.0 |
| NTIMIA4332 |  | 43.2078209 | -86.2245026 | HY LIFT L L C | MUSKEGON, MI | TCE |  |  |  | 1451.5 |
| NTIMIB1904 |  | 43.2170715 | -86.261322 | BRUNSWICK INDOOR RECREATION GROUP | MUSKEGON, MI | MC | 35117.1 |  |  |  |
| NTIMIB2289 |  | 41.8929214 | -84.0227432 | AGET MANUFACTURING COMPANY | ADRIAN, MI | TCE |  |  |  | 5107.4 |
| NTIMIB4096 |  | 41.8427505 | -85.6630936 | OWENS ILLINOIS CLOSURE, INC. | CONSTANTINE, MI | TCE |  |  |  | 7772.6 |
| NTIMIB4538 |  | 42.9239082 | -85.7012024 | BLACKMER | GRAND RAPIDS, MI | TCE |  |  |  | 36.3 |
| NTIMIB6220 |  | 42.5918808 | -82.8647003 | SELFRIDGE PLATING INC | HARRISON TWP, MI | TCE |  |  |  | 4254.7 |
| NTIMIB7018 |  | 42.4810905 | -83.4818726 | GENERAL FILTERS, INC. | NOVI, MI | TCE |  |  |  | 1814.4 |
| NTIMIM4403 |  | 42.3268013 | -83.418602 | D-N-R, INC. | WESTLAND, MI | TCE |  |  |  | 6311.3 |
| NTIMIM4607 |  | 42.1902885 | -83.1677017 | DETROIT TUBULAR RIVET INC. | WYANDOTTE, MI | MC | 7484.3 |  |  |  |
| NTIMIN5540 |  | 42.0922508 | -86.4196091 | TECH NICKEL INC | BENTON HARBOR, MI | TCE |  |  |  | 3559.5 |
| NTIMIN5733 |  | 42.5276108 | -83.0878601 | EAST LIND HEAT TREAT, INC | MADISON HTS, MI | TCE |  |  |  | 1518.6 |
| NTIMIN6173 |  | 45.2948799 | -85.2528381 | DME CO | CHARLEVOIX, MI | PCE |  | 1379.7 |  |  |
| NTIMIN6646 |  | 42.9963989 | -84.2153397 | OWOSSO GRAPHIC ARTS | OWOSSO, MI | TCE |  |  |  | 604.2 |
| NTIMIN6660 |  | 42.5064316 | -83.1177368 | STANHOPE TOOL, INC. | MADISON HTS, MI | TCE |  |  |  | 302.1 |
| NTIMN123294 |  | 44.9351997 | -93.0756989 | Viking Drill & Tool Inc | ST. PAUL, MN | TCE |  |  |  | 2950.6 |
| NTIMN1429 |  | 44.1731987 | -94.0457993 | MICO Inc | NORTH MANKATO, MN | MC | 4173.0 |  |  |  |
| NTIMN2713900 |  | 44.785099 | -93.5084 | ADC Telecommunications Inc - Shakopee | SHAKOPEE, MN | MC | 2819.1 |  |  |  |
| NTIMNT$8855 |  | 45.0834007 | -93.3891983 | Thomas Engineering Co | BROOKLYN PARK, MN | TCE |  |  |  | 3622.9 |
| NTIMNT$8860 |  | 45.1027985 | -93.2661972 | Larsen's Manufacturing | FRIDLEY, MN | TCE |  |  |  | 7487.0 |
| NTIMS025298 |  | 33.5889015 | -88.6496964 | BRYAN FOODS INC | WEST POINT, MS | PCE |  | 0.9 |  |  |
| NTIMS059302 |  | 30.5613995 | -88.8171997 | FERSON OPTICS, INC | OCEAN SPRINGS, MS | MC,TCE | 6531.7 |  |  | 16057.2 |
| NTINC787 |  | 35.6013908 | -82.3688889 | KEARFOTT | Black Mountain, NC | TCE |  |  |  | 1.6 |
| NTINJNJ34410 |  | 40.5740128 | -74.4079285 | AXIL CORP | SO. PLAINFIELD, NJ | MC | 170.1 |  |  |  |
| NTINM0031 |  | 32.2714005 | -106.953499 | Metal Parts Mfr | Las Cruces, NM | TCE |  |  |  | 44472.0 |
| NTINY013315 |  | 42.0924988 | -79.2244034 | CHAUTAUQUA HARDWARE CORP | JAMESTOWN, NY | TCE |  |  |  | 7257.5 |
| NTINY013316 |  | 42.1096992 | -79.206398 | VALEO INC ENGINE COOLING TRUCK DIVISION | JAMESTOWN, NY | PCE |  | 191.4 |  |  |
| NTINY2038 |  | 40.7647514 | -73.2841339 | A & M MANUFACTURING CO PROPERTY | BAY SHORE, NY | TCE |  |  |  | 13526.1 |
| NTINY3333600 |  | 41.4011002 | -73.9649963 | US MILITARY ACADEMY | WEST POINT, NY | PCE |  | 3.2 |  |  |
| NTINY8265400 |  | 43.2257996 | -77.4103012 | XEROX CORP | WEBSTER, NY | MC | 998.8 |  |  |  |
| NTIOH0829700 |  | 39.8171997 | -84.0369034 | US DOD WRIGHT-PATTERSON AFB OH | WPAFB, OH | PCE |  | 226.8 |  |  |
| NTIOH0857730 |  | 39.8156013 | -84.1800995 | WALL COLMONOY | DAYTON, OH | TCE |  |  |  | 4535.9 |
| NTIOH0857770 |  | 39.7958984 | -84.1340027 | MULLINS RUBBER PRODUCTS, INC. | DAYTON, OH | TCE |  |  |  | 9525.4 |
| NTIOHRR239 |  | 39.9645996 | -83.6173019 | UNITED FIBERGLASS OF AMERICA, INC. | SOUTH VIENNA, OH | MC | 1360.8 |  |  |  |
| NTIOHRR255 |  | 39.8209 | -84.0067978 | STADCO AUTOMATICS DIV. | FAIRBORN, OH | TCE |  |  |  | 2721.6 |
| NTIOHRR298 |  | 39.7984009 | -83.8905029 | VERNAY LABORATORIES, INC. S COLLEGE | YELLOW SPRINGS, OH | PCE |  | 226.8 |  |  |
| NTIOHRR299 |  | 39.8028984 | -83.9052963 | VERNAY LABORATORIES, INC. DAYTON ST | YELLOW SPRINGS, OH | PCE,TCE |  | 1451.5 |  | 1179.3 |
| NTIOHRR343 |  | 40.0396004 | -84.1992035 | HOBART CABINET | TROY, OH | PCE |  | 6350.3 |  |  |
| NTIOHRR364 |  | 39.967701 | -84.1986008 | CAPTOR CORPORATION | TIPP CITY, OH | TCE |  |  |  | 2268.0 |
| NTIOHRR385 |  | 39.7817993 | -84.1815033 | B-N PLATING | DAYTON, OH | TCE |  |  |  | 3810.2 |
| NTIOHRR386 |  | 39.7695999 | -84.1492004 | STACO ENERGY PRODUCTS, INC. | DAYTON, OH | PCE |  | 1360.8 |  |  |
| NTIOHRR501 |  | 39.75 | -84.2699966 | HARTZELL MANUFACTURING CO. INC. | MIAMISBURG, OH | PCE |  | 3628.7 |  |  |
| NTIOHRR524 |  | 39.75 | -84.2699966 | TRW SENSORS & COMPONENTS | VANDALIA, OH | TCE |  |  |  | 780.2 |
| NTIOHRR577 |  | 39.7909012 | -84.1931 | ALPINE PRODUCTS MFG CO. INC. | DAYTON, OH | TCE |  |  |  | 4717.4 |
| NTIOHT$6556 |  | 39.9072227 | -84.2074966 | MCCAULEY PROPELLER SYS. | VANDALIA, OH | MC,PCE | 6713.2 | 1814.4 |  |  |
| NTIOHT$6567 |  | 39.7630005 | -84.1798019 | WINSTON HEAT TREATING INC. | DAYTON, OH | PCE |  | 4082.3 |  |  |
| NTIOHT$6598 |  | 39.6534004 | -84.2433014 | DAYTON PROGRESS | DAYTON, OH | TCE |  |  |  | 4989.5 |
| NTIOK1229 |  | 35.4719009 | -98.0025024 | Cimarron Aircraft Corp. |  | MC | 4898.8 |  |  |  |
| NTIOK2785 |  | 35.7280998 | -95.3714981 | The Yaffe Companies, Inc. |  | TCE |  |  |  | 1496.9 |
| NTIOK4206 |  | 35.9518013 | -95.8890991 | Limco Airepair | Tulsa, OK | TCE |  |  |  | 3538.0 |
| NTIOK4252 |  | 35.4774017 | -97.6885986 | Pro-Fab, Inc. | Oklahoma City, OK | TCE |  |  |  | 907.2 |
| NTIPA12304-3 |  | 41.8684998 | -79.1502991 | OSRAM SYLVANIA PROD /WARREN PLT | WARREN, PA | TCE |  |  |  | 1088.6 |
| NTIPA13304-3 |  | 39.9676018 | -76.7546005 | OSRAM SYLVANIA PROD /YORK BASE PROD PLT | YORK, PA | TCE |  |  |  | 5533.8 |
| NTIPA14-1682 |  | 40.2529984 | -75.2798004 | AMETEK INC/SELLERSVILLE | SELLERSVILLE, PA | TCE |  |  |  | 2268.0 |
| NTIPA2098 |  | 40.4219017 | -79.8884964 | KOPP GLASS, INCORPORATED. | PITTSBURGH, PA | TCE |  |  |  | 737.1 |
| NTIPA2187 |  | 41.1194992 | -78.7612 | INVENSYS ENERGY METE/PLT 1 LIBERTY BLVD | DUBOIS, PA | TCE |  |  |  | 3356.6 |
| NTIPA2244 |  | 40.0262985 | -75.031601 | MODEL FINISHING CO | PHILADELPHIA, PA | TCE |  |  |  | 1088.6 |
| NTIPA23-0419 |  | 40.1519012 | -75.013298 | BOEKEL IND INC/FEASTERVILLE | FEASTERVILLE, PA | TCE |  |  |  | 3265.9 |
| NTIPA23-2947 |  | 40.1069984 | -79.5840988 | DYNAMIC METAL FORMIN/SCOTTDALE PLT | SCOTTDALE, PA | TCE |  |  |  | 30662.8 |
| NTIPA25-0932 |  | 41.769001 | -78.0835037 | EMPORIUM SPECIALTIES/FOSTER AVE PLT | AUSTIN, PA | TCE |  |  |  | 2721.6 |
| NTIPA25-0946 |  | 41.0163994 | -80.4167023 | FLOWLINE DIV MARKOVI/NEW CASTLE | NEW CASTLE, PA | TCE |  |  |  | 13789.2 |
| NTIPA25-1054 |  | 40.2971001 | -79.3917007 | LATRONICS CORP/LATROBE PLT | LATROBE, PA | TCE |  |  |  | 4535.9 |
| NTIPA25-1355 |  | 41.7995987 | -78.6334 | KEYSTONE THERMOMETRI/MT JEWETT PLT | MT JEWETT, PA | TCE |  |  |  | 1451.5 |
| NTIPA25-1645 |  | 40.8718987 | -79.8395004 | CASTLE RUBBER CO/EAST BUTLER | EAST BUTLER, PA | TCE |  |  |  | 907.2 |
| NTIPA48-1100 |  | 40.2187996 | -75.2782974 | MUELLER STREAMLINE C/NORTH WALES | NORTH WALES, PA | MC | 44179.9 |  |  |  |
| NTIRCA036401 |  | 37.5041161 | -121.958046 | CHA INDUSTRIES | FREMONT, CA | TCA |  |  | 39.5 |  |
| NTIRCA038551 |  | 38.2070808 | -122.142082 | YOUNG PRODUCTS | SUISUN CITY, CA | TCA |  |  | 410.1 |  |
| NTIRCA303707 |  | 37.428627 | -122.097664 | BELL INDUSTRIES, PRECISION MET | MOUNTAIN VIEW, CA | TCE |  |  |  | 317.1 |
| NTIRCA310521 |  | 37.5109215 | -122.263443 | COMMUNICATIONS & POWER INDUSTR | SAN CARLOS, CA | TCA,TCE |  |  | 1838.3 | 1133.7 |
| NTIRCA310581 |  | 37.7794991 | -122.242325 | REGENCY RESTORATION & ANTIQUES | OAKLAND, CA | MC | 180.5 |  |  |  |
| NTIRCA310599 |  | 37.7673912 | -122.219162 | SANTANA'S FURNITURE REFINISH | OAKLAND, CA | MC | 827.2 |  |  |  |
| NTIRCA311021 |  | 37.3789902 | -121.97084 | MICREL SYNERGY SEMICONDUCTOR | SANTA CLARA, CA | MC | 7.3 |  |  |  |
| NTIRCA311178 |  | 37.4002113 | -121.915535 | LOCKHEED MARTIN FAIRCHILD SYST | MILPITAS, CA | TCA |  |  | 7.6 |  |
| NTIRCA311226 |  | 38.0133667 | -122.037102 | STRIPPING WORKSHOP SERVICE GRO | CONCORD, CA | MC | 3308.8 |  |  |  |
| NTIRCA311329 |  | 37.41259 | -121.953941 | SUPERTEX INC | SAN JOSE, CA | TCA |  |  | 9.0 |  |
| NTIRMN300066 |  | 45.0634995 | -93.2683029 | Kurt Manufacturing Inc - Main St | FRIDLEY, MN | TCE |  |  |  | 1147.4 |
| NTIRMN301074 |  | 44.9548988 | -93.2266998 | Hiawatha Metalcraft Inc | MINNEAPOLIS, MN | TCE |  |  |  | 4176.2 |
| NTIRMN500041 |  | 44.8961983 | -94.3800964 | New Dimension Plating | HUTCHINSON, MN | TCE |  |  |  | 2109.2 |
| NTIRSC0-0021 |  | 34.2062912 | -82.126564 | KENDALL:HEALTH CARE | GREENWOOD, SC | PCE |  | 0.5 |  |  |
| NTIRSC156063 |  | 33.9453125 | -81.1211472 | EAGLE AVIATION INC | WEST COLUMBIA, SC | MC | 36.3 |  |  |  |
| NTISC2435 |  | 34.6774902 | -82.1973877 | VAN DORN DEMAG CORP | FOUNTAIN INN, SC | TCE |  |  |  | 1826.2 |
| NTISCT$3360 |  | 34.1258202 | -80.8702698 | FN MANUFACTURING | COLUMBIA, SC | TCE |  |  |  | 1946.8 |
| NTIT$FNP1184 |  | 45.5712013 | -122.598999 | Portland Willamette | PORTLAND, OR | TCE |  |  |  | 8890.4 |
| NTITN0470 |  | 35.0195999 | -85.2972031 | CHATTANOOGA ARMATURE WORKS, INC. | CHATTANOOGA, TN | TCE |  |  |  | 471.7 |
| NTITXT$11375 |  | 32.9361687 | -97.0989838 | FOUR SEASONDIVISION OF | GRAPEVINE, TX | TCE |  |  |  | 7264.1 |
| NTITXT$11857 |  | 29.8199997 | -98.3199997 | FLEXTRONICSENCLOSURES INC | SAN ANTONIO, TX | TCE |  |  |  | 13991.3 |
| NTIVA6500005 |  | 37.0180016 | -76.3242035 | Maida Development Company | Hampton, VA | PCE |  | 997.9 |  |  |
| NTIWA10203 |  | 47.7988434 | -122.655212 | Seattle Orthopedic Group Inc | Poulsbo, WA | MC | 5488.5 |  |  |  |
| NTIWA13117 |  | 47.2821999 | -122.238403 | Boeing Commercial Airplane (Auburn) | Auburn, WA | MC,PCE | 233.1 | 898.6 |  |  |
| NTIWA13120 |  | 47.9196014 | -122.277199 | Boeing Commercial Airplane Group - Everett | Everett, WA | TCE |  |  |  | 49166.2 |
| NTIWA14092 |  | 47.4056969 | -122.248375 | Web Press Corporation | Kent, WA | TCE |  |  |  | 2220.3 |
| NTIWA15119 |  | 47.8967056 | -122.273346 | Goodrich Aviation | Everett, WA | MC | 210.0 |  |  |  |
| NTIWA16328 |  | 47.3959999 | -122.233398 | Protective Coatings Inc | Kent, WA | TCE |  |  |  | 5644.0 |
| NTIWA17771 |  | 47.0932503 | -122.354286 | Boeing Commercial Airplane (Frederickson) | Puyallup, WA | MC,PCE | 63.5 | 95.3 |  |  |
| NTIWA28563 |  | 47.6723442 | -122.094231 | Genie Industries Inc (Main Campus) | Redmond, WA | MC | 89.8 |  |  |  |
| NTIWI1280497 |  | 43.0817032 | -88.8957748 | FIBERDOME INC., PLANT #2 | LAKE MILLS, WI | MC | 276.2 |  |  |  |
| NTIWI1280585 |  | 43.0649643 | -88.9217224 | FIBERDOME INC-PLANT #1 | LAKE MILLS, WI | MC | 251.3 |  |  |  |
| NTIWI1541294 |  | 42.7731514 | -89.2994843 | Southern Wisconsin Metal Fabrication, Inc. | EVANSVILLE, WI | TCE |  |  |  | 1333.6 |
| NTIWI2410141 |  | 43.0075607 | -87.9738007 | G E MEDICAL SYSTEMS: ELECTRIC AVE. FACILITY | WEST MILWAUKEE, WI | MC | 434.0 |  |  |  |
| NTIWI2410173 |  | 43.1487389 | -88.0130844 | PERLICK CORPORATION | MILWAUKEE, WI | TCE |  |  |  | 101.6 |
| NTIWI2410342 |  | 43.0187645 | -87.913002 | ALLEN-BRADLEY | MILWAUKEE, WI | MC | 1763.1 |  |  |  |
| NTIWI2410368 |  | 43.0489159 | -87.9157715 | MILWAUKEE PLATING CO | MILWAUKEE, WI | TCE |  |  |  | 889.0 |
| NTIWI2416654 |  | 42.8623619 | -87.9874954 | General Automotive Manufacturing, LLC-W. Franklin | FRANKLIN, WI | TCE |  |  |  | 2721.6 |
| NTIWI2419617 |  | 42.8672256 | -87.9804535 | General Automotive Manufacturing, LLC-W. Airway | FRANKLIN, WI | TCE |  |  |  | 7438.9 |
| NTIWI2460526 |  | 43.3756828 | -87.8826523 | MOLDED DIMENSIONS | PORT WASHINGTON, WI | TCE |  |  |  | 2086.5 |
| NTIWI2520097 |  | 42.7478371 | -87.8010864 | E C STYBERG ENGINEERING CO INC | RACINE, WI | TCE |  |  |  | 2268.0 |
| NTIWI2650061 |  | 42.7904167 | -88.389389 | CRUCIBLE MATERIALS CORP TRENT TUBE PLT 2 & 3 | EAST TROY, WI | TCE |  |  |  | 48806.5 |
| NTIWI2680147 |  | 43.0858841 | -88.2650146 | DYNEX-RIVETT, INC | PEWAUKEE, WI | TCE |  |  |  | 3356.6 |
| NTIWI2681860 |  | 43.1085014 | -88.4842987 | PREMOLD CORPORATION | OCONOMOWOC, WI | TCE |  |  |  | 1736.4 |
| NTIWI2682381 |  | 43.0478363 | -88.1833191 | Casting Impregnators of Wisconsin, Inc. | WAUKESHA, WI | TCE |  |  |  | 3084.4 |
| NTIWI4380172 |  | 45.0793724 | -87.6433258 | WINSERT INC | MARINETTE, WI | TCE |  |  |  | 2903.0 |
| NTIWI4711097 |  | 44.1637383 | -88.4746628 | Voith Sulzer Paper Technology | NEENAH, WI | TCE |  |  |  | 4173.0 |
| NTIWI6030598 |  | 45.5438004 | -92.0174179 | AMERICAN TOOL COMPANY (FORMERLY IRWIN) | CUMBERLAND, WI | TCE |  |  |  | 2540.1 |
| NTIWI7440095 |  | 45.6319351 | -89.3939056 | PRECISION TWIST DRILL CO - RHINELANDER | RHINELANDER, WI | TCE |  |  |  | 7529.6 |

1 MC = Methylene Chloride; PCE = Tetrachloroethylene (perchloroethylene); TCA = trichloroethane (is not a carcinogen so does not contribute to facility-total MC-equivalent emissions in Exhibit E-1); TCE = trichloroethylene.

Exhibit B-2

Selected Fields from the 2002 National Emissions Inventory Data for All Halogenated Solvent Cleaning Facilities

| Modeling ID | Lat | Lon | Facility Name | City, State | Chemicals | MC Emission Rate (kg/yr) 1 | TCA Emission Rate (kg/yr) 1 | PCE Emission Rate (kg/yr) 1 | TCE Emission Rate (kg/yr) 1 | C Tetrachloride Emission Rate (kg/yr) 1 | Chloroform Emission Rate (kg/yr) 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| NEI310 | 36.99843 | -76.45188 | NEWPORT NEWS SHIPBUILDING | NEWPORT NEWS, VA | TCA |  | 27.2 |  |  |  |  |
| NEI946 | 39.64686 | -104.9996 | COLORADO MOLDED PRODUCTS CO | ENGLEWOOD, CO | TCE |  |  |  | 3991.6 |  |  |
| NEI965 | 40.0621 | -105.2065 | COMPLEX TOOLING & MOLDING INC | BOULDER, CO | MC | 225.4 |  |  |  |  |  |
| NEI968 | 40.14967 | -105.1129 | NYPRO COLORADO INC | LONGMONT, CO | MC | 97.6 |  |  |  |  |  |
| NEI1367 | 39.69041 | -104.9908 | CYCLO MANUFACTURING CO | DENVER, CO | MC | 136.1 |  |  |  |  |  |
| NEI1608 | 39.75224 | -104.8766 | STANLEY AVIATION CORP | AURORA, CO | TCE |  |  |  | 1876.8 |  |  |
| NEI1830 | 38.80888 | -104.7253 | BOYD LIGHTING CO | COLORADO SPRINGS, CO | PCE |  |  | 1509.1 |  |  |  |
| NEI2162 | 38.27723 | -104.4889 | MCDONNELL DOUGLAS ASTRONAUTICS CO | PUEBLO, CO | TCA |  | 454.0 |  |  |  |  |
| NEI2733 | 42.88167 | -71.17889 | JOHNSON & JOHNSTON ASSOC. INC. | HAMPSTEAD, NH | TCE |  |  |  | 15527.4 |  |  |
| NEI3606 | 40.42414 | -104.6983 | YE OLDE STRIPPE SHOPPE | GREELEY, CO | MC | 342.4 |  |  |  |  |  |
| NEI3618 | 39.80356 | -104.9312 | STEWART & STEVENSON POWER INC | COMMERCE CITY, CO | TCA |  | 10.4 |  |  |  |  |
| NEI4694 | 40.14424 | -105.1404 | DISPLAYTECH INC | LONGMONT, CO | MC | 92.7 |  |  |  |  |  |
| NEI4855 | 40.08714 | -105.182 | FRONT RANGE TOOLING INC | LONGMONT, CO | MC | 23.8 |  |  |  |  |  |
| NEI5372 | 40.69201 | -78.22884 | CHICAGO RIVET & MACH/TYRONE PLT | TYRONE, PA | TCE |  |  |  | 21681.7 |  |  |
| NEI5410 | 40.10674 | -75.34331 | TUBE METHODS INC/BRIDGEPORT | BRIDGEPORT, PA | TCE |  |  |  | 12310.5 |  |  |
| NEI5994 | 30.02467 | -89.91687 | LOCKHEED MARTIN CORP/MICHOUD | NEW ORLEANS, LA | TCE |  |  |  | 93.0 |  |  |
| NEI6135 | 29.9549 | -90.15045 | GULF WIRE CORP | NEW ORLEANS, LA | TCE |  |  |  | 12497.4 |  |  |
| NEI6225 | 41.65079 | -71.47511 | STANLEY-BOSTITCH, INC. (EG) | EAST GREENWICH, RI | MC | 7724.7 |  |  |  |  |  |
| NEI6360 | 41.53556 | -73.0325 | SOMERS THIN STRIP | WATERBURY, CT | MC | 52519.6 |  |  |  |  |  |
| NEI6536 | 32.74194 | -96.97972 | VOUGHT JEFFERSON ST FACIL | DALLAS, TX | TCE |  |  |  | 114.1 |  |  |
| NEI6596 | 32.28917 | -95.25361 | SPINE FIN MACHINE | TYLER, TX | TCE |  |  |  | 11750.3 |  |  |
| NEI6865 | 32.34 | -102.5539 | ANDREWS PLANT | ANDREWS, TX | MC | 816.5 |  |  |  |  |  |
| NEI6954 | 42.06778 | -79.15305 | KEYWELL L.L.C. VAC AIR DIV. | FREWSBURG, NY | TCE |  |  |  | 5891.7 |  |  |
| NEI7024 | 41.42125 | -78.5692 | KEYSTONE POWDERED METAL CO | SAINT MARYS, PA | TCE |  |  |  | 12882.0 |  |  |
| NEI7025 | 41.55556 | -78.58336 | KEYSTONE THERMOMETRICS/WINDFALL RD | SAINT MARYS, PA | TCE |  |  |  | 1771.1 |  |  |
| NEI7068 | 41.01667 | -80.41665 | FLOWLINE DIV MARKOVI/NEW CASTLE | NEW CASTLE, PA | TCE |  |  |  | 8709.0 |  |  |
| NEI7069 | 41.35553 | -80.41124 | SALEM TUBE INC/SALEM TUBE INC | GREENVILLE, PA | TCE |  |  |  | 55337.5 |  |  |
| NEI7092 | 41.87746 | -80.12183 | PENN UNION CORP/EDINBORO | EDINBORO, PA | PCE |  |  | 22452.8 |  |  |  |
| NEI7150 | 29.67056 | -96.79028 | WEIMER PLANT | WEIMER, TX | TCE |  |  |  | 1300.4 |  |  |
| NEI7172 | 39.90145 | -76.62891 | GICHNER SHELTER SYS/DALLASTOWN PLT | DALLASTOWN, PA | TCE |  |  |  | 25854.8 |  |  |
| NEI7218 | 40.80267 | -76.44722 | ARCOS IND LLC/MT CARMEL PLT | MOUNT CARMEL, PA | PCE |  |  | 3719.5 |  |  |  |
| NEI7323 | 40.10175 | -75.13891 | SPS TECH INC/ABINGTON | JENKINTOWN, PA | TCE |  |  |  | 635.0 |  |  |
| NEI7331 | 39.93637 | -75.18577 | SEAGULL LIGHTING | PHILADELPHIA, PA | TCE |  |  |  | 11140.2 |  |  |
| NEI7345 | 40.16703 | -75.33775 | HANDY & HARMAN TUBE /EAST NORRITON | NORRISTOWN, PA | TCE |  |  |  | 45503.3 |  |  |
| NEI7347 | 40.23332 | -75.55283 | UNIFORM TUBES INC/COLLEGEVILLE | COLLEGEVILLE, PA | TCA, TCE |  | 16624.3 |  | 49060.5 |  |  |
| NEI7348 | 40.1867 | -75.43652 | SUPERIOR TUBE CO/LOWER PROVIDENCE | COLLEGEVILLE, PA | TCE |  |  |  | 63775.1 |  |  |
| NEI7350 | 40.25787 | -75.32925 | PENN FISHING TACKLE MFG/TOWAMENCIN | KULPSVILLE, PA | MC | 8527.5 |  |  |  |  |  |
| NEI7352 | 40.21908 | -75.2783 | PRECISION TUBE COMPANY | NORTH WALES, PA | MC | 8709.0 |  |  |  |  |  |
| NEI7365 | 40.32118 | -76.02576 | WILLIAMS METALFINISHING/SINKING SPRING | SINKING SPRING, PA | TCE |  |  |  | 5515.7 |  |  |
| NEI7367 | 40.32316 | -75.94105 | BALDWIN HDWR CORP/READING PLT | READING, PA | TCE |  |  |  | 66587.3 |  |  |
| NEI7368 | 40.35887 | -75.93742 | CARPENTER TECH CORP/READING PLT | READING, PA | TCE |  |  |  | 1712.8 |  |  |
| NEI7573 | 32.89139 | -96.70278 | MARLOW INDUSTRIES | DALLAS, TX | TCE |  |  |  | 680.4 |  |  |
| NEI7752 | 31.66581 | -94.66142 | GASKET & SEAL MFG FAC | NACOGDOCHES, TX | PCE |  |  | 90.7 |  |  |  |
| NEI7945 | 34.79938 | -82.36212 | HITACHI ELECTRONIC | MAULDIN, SC | TCE |  |  |  | 3039.1 |  |  |
| NEI7956 | 34.96109 | -82.44194 | SAINT GOBAIN ABRASIVES | TRAVELERS REST, SC | PCE |  |  | 6930.0 |  |  |  |
| NEI8011 | 28.41908 | -96.67897 | SEADRIFT PLANT | SEADRIFT, TX | TCE |  |  |  | 10.0 |  |  |
| NEI8259 | 29.72667 | -95.0775 | OXY VINYLS, L.P. | LA PORTE, TX | TCA |  | 0.7 |  |  |  |  |
| NEI8273 | 30.22677 | -81.67018 | UNITED STATES NAVY | JACKSONVILLE, FL | MC, TCA | 3728.1 | 9.3 |  |  |  |  |
| NEI8297 | 28.31114 | -80.70934 | HYDRO ALUMINUM | ROCKLEDGE, FL | TCE |  |  |  | 5506.6 |  |  |
| NEI8320 | 25.92684 | -80.25616 | GOODRICH CORPORATION | OPA-LOCKA, FL | TCE |  |  |  | 19776.6 |  |  |
| NEI8346 | 29.32523 | -81.11544 | HUDSON TOOL & DIE CO | ORMOND BEACH, FL | TCE |  |  |  | 21763.4 |  |  |
| NEI8604 | 30.54928 | -88.13732 | TAYLOR WHARTON | THEODORE, AL | TCE |  |  |  | 5080.2 |  |  |
| NEI10885 | 32.83861 | -96.84417 | GULFSTREAM AEROSPACE CORP. | DALLAS, TX | MC | 9.1 |  |  |  |  |  |
| NEI11059 | 29.72833 | -95.15667 | PASADENA PLANT | PASADENA, TX | TCA, PCE |  | 0.6 | 0.6 |  |  |  |
| NEI11106 | 33.8249 | -89.79833 | OUTOKUMPU HEATCRAFT LLC, COMMERCIAL COIL | GRENADA, MS | TCE |  |  |  | 37812.5 |  |  |
| NEI11188 | 32.71556 | -97.03083 | MARSHALL STREET FACILITY | GRAND PRAIRIE, TX | MC, TCE | 30.5 |  |  | 245.7 |  |  |
| NEI11243 | 37.83115 | -85.47173 | JIDECO OF BARDSTOWN, INC | BARDSTOWN, KY | TCA |  | 1521.6 |  |  |  |  |
| NEI11248 | 38.2098 | -85.22627 | ROLL FORMING CORP | SHELBYVILLE, KY | TCE |  |  |  | 4490.6 |  |  |
| NEI11259 | 37.77733 | -84.85289 | MODINE MANUFACTURING CO | HARRODSBURG, KY | TCE |  |  |  | 9452.9 |  |  |
| NEI11275 | 37.69478 | -84.2621 | OKONITE COMPANY THE | RICHMOND, KY | MC | 30.4 |  |  |  |  |  |
| NEI11295 | 29.03163 | -95.4029 | PLANT B | CLUTE, TX | TCA, PCE |  | 1250.1 | 17.7 |  |  |  |
| NEI11307 | 39.03058 | -84.44463 | FISCHER SPECIAL MFG CO | COLD SPRING, KY | TCE |  |  |  | 5211.4 |  |  |
| NEI11344 | 36.73608 | -86.56212 | DANA CORPORATION | FRANKLIN, KY | TCE |  |  |  | 10102.4 |  |  |
| NEI11349 | 36.87552 | -87.50824 | EBONITE INTERNATIONAL | HOPKINSVILLE, KY | MC | 12258.6 |  |  |  |  |  |
| NEI11368 | 37.69452 | -87.87445 | RAYLOC | MORGANFIELD, KY | TCE |  |  |  | 22407.5 |  |  |
| NEI11474 | 27.88361 | -97.24139 | INGLESIDE PLANT | INGLESIDE, TX | TCE |  |  |  | 616.9 |  |  |
| NEI11517 | 41.48333 | -81.66695 | BF GOODRICH LANDING GEAR DIVISION - PLATING OPERAT | CLEVELAND, OH | TCE |  |  |  | 6047.0 |  |  |
| NEI11519 | 41.58028 | -81.53056 | LINDERME TUBE COMPANY (THE) | CLEVELAND, OH | TCE |  |  |  | 31116.4 |  |  |
| NEI11526 | 41.39953 | -81.47388 | TOOL-DIE ENGINEERING COMPANY (TDE GROUP, INCORPORA | SOLON, OH | PCE |  |  | 1683.6 |  |  |  |
| NEI11648 | 39.8915 | -83.725 | TRUTEC INDUSTRIES, INC. | SPRINGFIELD, OH | TCE |  |  |  | 69490.3 |  |  |
| NEI11709 | 39.90413 | -86.25836 | EAR SPECIALTY COMPOSITES & AEARO COMPANY | INDIANAPOLIS, IN | MC, TCA | 272.2 | 5479.4 |  |  |  |  |
| NEI11790 | 39.12583 | -85.96195 | RIGHTWAY FASTENERS INC | COLUMBUS, IN | MC | 14333.5 |  |  |  |  |  |
| NEI11809 | 32.83139 | -97.31778 | AIR CONTIONING | FORT WORTH, TX | MC | 24403.3 |  |  |  |  |  |
| NEI11810 | 37.97932 | -87.58521 | CRADDOCK FINISHING CORPORATION | EVANSVILLE, IN | TCE |  |  |  | 237.1 |  |  |
| NEI11865 | 42.32589 | -83.87903 | DAPCO INDUSTRIES | DEXTER, MI | MC | 6574.2 |  |  |  |  |  |
| NEI11916 | 42.98983 | -84.20459 | MOTOR PRODUCTS - A DIVISION OF ALLIED MOTION TECH. | OWOSSO, MI | TCE |  |  |  | 2332.8 |  |  |
| NEI11984 | 43.21446 | -86.24608 | DANA CORPORATION - SANFORD STREET FACILITY | MUSKEGON, MI | TCE |  |  |  | 6889.6 |  |  |
| NEI11985 | 43.23265 | -86.20768 | DANA CORPORATION - HARVEY STREET FACILITY | MUSKEGON, MI | TCE |  |  |  | 2368.5 |  |  |
| NEI11994 | 42.94509 | -85.68465 | KEELER BRASS COMPANY | GRAND RAPIDS, MI | MC, TCE | 9220.6 |  |  | 25723.2 |  |  |
| NEI12240 | 41.54148 | -90.46319 | ALCOA INC. | BETTENDORF, IA | PCE |  |  | 48010.5 |  |  |  |
| NEI12314 | 44.9492 | -93.169 | CO-OPERATIVE PLATING CO | ST. PAUL, MN | TCE |  |  |  | 2560.4 |  |  |
| NEI12320 | 44.8801 | -93.2053 | NORTHWEST AIRLINES INC - MPLS/ST PAUL | MINNEAPOLIS, MN | TCA, TCE |  | 7.4 |  | 23093.6 |  |  |
| NEI12333 | 44.8587 | -93.5292 | ROBERTS AUTOMATIC PRODUCTS | CHANHASSEN, MN | MC | 3979.0 |  |  |  |  |  |
| NEI12348 | 44.9496 | -93.2764 | NICO PRODUCTS INC | MINNEAPOLIS, MN | TCE |  |  |  | 14197.4 |  |  |
| NEI12350 | 44.9826 | -93.2182 | GREATBATCH - GLOBE TOOL INC | MINNEAPOLIS, MN | TCE |  |  |  | 11856.9 |  |  |
| NEI12355 | 45 | -93.3603 | HONEYWELL - GOLDEN VALLEY | GOLDEN VALLEY, MN | TCE |  |  |  | 8240.0 |  |  |
| NEI12422 | 27.6975 | -97.27472 | CORPUS CHRISTI ARMY DEPOT | CORPUS CHRISTI, TX | MC, TCE | 84.7 |  |  | 121.5 |  |  |
| NEI12595 | 32.77278 | -97.05917 | PLANT 5A | GRAND PRAIRIE, TX | MC, PCE | 548.8 |  | 33360.9 |  |  |  |
| NEI12727 | 39.08222 | -94.73583 | MERIDIAN AUTOMOTIVE SYSTEMS, INC. | KANSAS CITY, KS | TCE |  |  |  | 2893.9 |  |  |
| NEI12750 | 37.74833 | -97.3175 | COLEMAN CO., INC. (THE) | WICHITA, KS | MC | 286.0 |  |  |  |  |  |
| NEI12927 | 35.46965 | -97.71279 | XEROX CORP | YUKON, OK | MC | 72.6 |  |  |  |  |  |
| NEI12930 | 35.42162 | -97.39194 | TINKER AFB US AIR FORCE LOGISTICS CTR | MIDWEST CITY, OK | MC, PCE | 5713.4 |  | 7299.2 |  |  |  |
| NEI12973 | 36.17814 | -95.85427 | NORDAM GROUP INC | TULSA, OK | TCE |  |  |  | 3193.3 |  |  |
| NEI12974 | 36.37365 | -95.82977 | HONEYWELL INC | TULSA, OK | PCE |  |  | 1079.5 |  |  |  |
| NEI13038 | 32.81583 | -96.93611 | OWENS CORNING | IRVING, TX | PCE |  |  | 2.9 |  |  |  |
| NEI13146 | 39.65108 | -105.0288 | OAKLEY INDUSTRIES INC OAKLEY TUBE DIV | SHERIDAN, CO | TCE |  |  |  | 2041.2 |  |  |
| NEI13238 | 29.70194 | -95.39778 | TEXAS MEDICAL CENTER | HOUSTON, TX | PCE |  |  | 0.2 |  |  |  |
| NEI13309 | 32.77175 | -96.65382 | TILE AND OIL FIELD PRODUCTS | MESQUITE, TX | MC | 761.4 |  |  |  |  |  |
| NEI13336 | 45.54538 | -122.4674 | BOEING COMPANY (THE) | PORTLAND, OR | TCA, PCE, TCE |  | 9.1 | 4535.9 | 281.2 |  |  |
| NEI18329 | 33.63757 | -85.91969 | ANNISTON ARMY DEPOT | ANNISTON, AL | MC, TCE | 62686.5 |  |  | 30191.1 |  |  |
| NEI18760 | 37.7409 | -122.2061 | WORLD HEART INC | OAKLAND, CA | MC | 25.9 |  |  |  |  |  |
| NEI18906 | 37.67988 | -121.7646 | DOE-KAO SANDIA NATIONAL LABORA | LIVERMORE, CA | TCA, PCE |  | 235.1 | 42.8 |  |  |  |
| NEI18907 | 37.70995 | -121.927 | DOLD'S WORKSHOP | DUBLIN, CA | MC | 3008.0 |  |  |  |  |  |
| NEI18914 | 37.69019 | -121.9149 | DUBLIN SAN RAMON SERVICES DIST | PLEASANTON, CA | TCA |  | 99.0 |  |  |  |  |
| NEI19032 | 37.64331 | -122.1297 | HTB INC | HAYWARD, CA | TCE |  |  |  | 3649.8 |  |  |
| NEI19042 | 37.85566 | -122.2914 | INLITE CORPORATION | BERKELEY, CA | TCA |  | 1086.0 |  |  |  |  |
| NEI19053 | 37.77419 | -122.2492 | J D HARPE FURNITURE FINISHERS | ALAMEDA, CA | MC | 882.3 |  |  |  |  |  |
| NEI19067 | 37.6432 | -121.8819 | KAISER ALUMINUM & CHEMICAL COR | PLEASANTON, CA | TCA |  | 24.7 |  |  |  |  |
| NEI19090 | 37.8665 | -122.2988 | LAWRENCE BERKELEY NATIONAL LAB | BERKELEY, CA | TCA, TCE |  | 65.0 |  | 2.7 |  |  |
| NEI19091 | 37.69514 | -121.7087 | LAWRENCE LIVERMORE NATIONAL LA | LIVERMORE, CA | MC, TCA, TCE | 25.0 | 99.0 |  | 0.3 |  |  |
| NEI19512 | 39.19797 | -122.0283 | PIRELLI CABLE CORPORATION | COLUSA, CA | TCA |  | 3937.6 |  |  |  |  |
| NEI19793 | 37.92464 | -122.3602 | PILGRIM FIREPLACE EQUIPMENT CO | RICHMOND, CA | TCA |  | 147.2 |  |  |  |  |
| NEI19913 | 36.7518 | -119.724 | PACTIV CORPORATION | FRESNO, CA | TCA |  | 867.3 |  |  |  |  |
| NEI19914 | 36.73564 | -119.7604 | ATAPCO OFFICE PRODUCTS GROUP | FRESNO, CA | TCA |  | 226.8 |  |  |  |  |
| NEI19921 | 36.71212 | -119.7575 | CHAMPION PARTS WESTERN DIVISIO | FRESNO, CA | TCA |  | 34936.6 |  |  |  |  |
| NEI19927 | 36.50873 | -119.5491 | DEL MONTE FOODS PLANT NO. 25 | KINGSBURG, CA | MC | 77.5 |  |  |  |  |  |
| NEI19932 | 36.81781 | -119.9045 | FRUEHAUF TRAILER OPERATIONS | FRESNO, CA | MC | 4340.9 |  |  |  |  |  |
| NEI20225 | 33.91994 | -118.271 | AAA ADVANCE FINISHING, INC | LOS ANGELES, CA | TCA |  | 1639.3 |  |  |  |  |
| NEI20228 | 34.02997 | -118.371 | ABBOTT TRANSISTOR LABORATORIES | LOS ANGELES, CA | TCA |  | 3425.0 |  |  |  |  |
| NEI20230 | 33.80729 | -118.1634 | ACCURATE METAL FABRICATORS INC | SIGNAL HILL, CA | TCA |  | 1107.7 |  |  |  |  |
| NEI20231 | 33.89993 | -118.1611 | ACE CLEARWATER ENTER. | PARAMOUNT, CA | TCA |  | 2245.3 |  |  |  |  |
| NEI20232 | 33.86782 | -118.2442 | ACE CLEARWATER ENTERPRISES | TORRANCE, CA | TCA |  | 1197.5 |  |  |  |  |
| NEI20234 | 34.01997 | -117.961 | ACORN ENGINEERING CO | INDUSTRY, CA | TCA |  | 17770.9 |  |  |  |  |
| NEI20237 | 34.13275 | -118.2643 | ADAMS RITE SABRE INTERNATIONAL | GLENDALE, CA | PCE |  |  | 1010.6 |  |  |  |
| NEI20241 | 33.90916 | -118.3012 | ADVANCED COATING & SILKSCREENING INC | GARDENA, CA | TCA |  | 1558.4 |  |  |  |  |
| NEI20242 | 34.21508 | -118.4816 | AELCO CORP | VAN NUYS, CA | TCA |  | 4276.0 |  |  |  |  |
| NEI20243 | 34.10205 | -118.244 | AERO ENGINES INC | LOS ANGELES, CA | MC, TCA, TCE | 1331.3 | 6678.2 |  | 139.7 |  |  |
| NEI20245 | 34.11993 | -117.9211 | AEROJET GENCORP, AEROJET ELECT | AZUSA, CA | TCA |  | 1465.1 |  |  |  |  |
| NEI20246 | 33.93157 | -118.1215 | GENERAL DYNAMICS OTS (DOWNEY) INC | DOWNEY, CA | MC, TCA | 2235.3 | 1233.3 |  |  |  |  |
| NEI20247 | 33.88991 | -118.1711 | AEROSPACE ALUMINUM HEAT TREATI | PARAMOUNT, CA | TCA |  | 12886.5 |  |  |  |  |
| NEI20249 | 33.88201 | -118.2682 | AHF DUCOMMUN, INC | CARSON, CA | TCA |  | 277.1 |  |  |  |  |
| NEI20252 | 33.95967 | -118.0659 | AIR LIQUIDE AMERICAN CORP | SANTA FE SPRINGS, CA | TCA |  | 796.1 |  |  |  |  |
| NEI20253 | 34.15001 | -118.0711 | AIR LOGISTICS CORP | PASADENA, CA | TCA |  | 872.7 |  |  |  |  |
| NEI20256 | 34.22992 | -118.3611 | AIRCRAFT CYLINDER & TURBINE IN | SUN VALLEY, CA | PCE |  |  | 2447.9 |  |  |  |
| NEI20257 | 33.98998 | -118.2211 | AIRCRAFT X-RAY LABS INC | HUNTINGTON PARK, CA | TCA |  | 3805.6 |  |  |  |  |
| NEI20268 | 34.29997 | -118.4711 | ALLIED-SIGNAL OCEAN SYSTEMS | SYLMAR, CA | TCA |  | 18845.4 |  |  |  |  |
| NEI20272 | 33.88573 | -118.0179 | AMADA MFG AMERICA, INC | LA MIRADA, CA | PCE |  |  | 7630.3 |  |  |  |
| NEI20273 | 33.94022 | -118.4205 | AMERICAN AIRLINES INC (EIS USE | LOS ANGELES, CA | MC, TCA | 2689.2 | 9264.7 |  |  |  |  |
| NEI20276 | 34.26997 | -118.4311 | AMERICAN ETCHING & MFG CO | PACOIMA, CA | TCA, PCE |  | 151.5 | 1105.9 |  |  |  |
| NEI20284 | 33.84516 | -118.3412 | AMP INCORPORATED | TORRANCE, CA | MC, TCA | 7.0 | 2554.5 |  |  |  |  |
| NEI20286 | 33.93217 | -118.1674 | ANADITE INC | SOUTH GATE, CA | TCA |  | 4533.5 |  |  |  |  |
| NEI20294 | 33.98998 | -118.2211 | ANGELUS SANITARY CAN MACHINE C | VERNON, CA | TCA |  | 703.7 |  |  |  |  |
| NEI20317 | 34.06992 | -118.1711 | ARROWHEAD BRASS PROD. INC | LOS ANGELES, CA | PCE |  |  | 5767.9 |  |  |  |
| NEI20327 | 33.89542 | -118.2792 | ASSOC SPRING BARNES GRP INC,AS | GARDENA, CA | TCA |  | 528.0 |  |  |  |  |
| NEI20328 | 33.91994 | -118.1711 | ASTRO ALUMINUM TREATING CO INC | SOUTH GATE, CA | TCA |  | 38197.9 |  |  |  |  |
| NEI20335 | 34.14418 | -118.002 | AVERY DENNISON | AZUSA, CA | TCA |  | 13018.1 |  |  |  |  |
| NEI20336 | 34.17189 | -118.3148 | AVIBANK MFG INC | BURBANK, CA | TCA, PCE |  | 5265.5 | 4.0 |  |  |  |
| NEI20337 | 34.22626 | -118.3732 | AVX FILTERS CORP | SUN VALLEY, CA | MC, TCA | 759.8 | 1313.1 |  |  |  |  |
| NEI20348 | 34.20831 | -118.4446 | BW/IP INTERNATIONAL INC | VAN NUYS, CA | TCA |  | 832.1 |  |  |  |  |
| NEI20353 | 34.02992 | -118.431 | BARLOW SPECIALTY ADVERTISING I | LOS ANGELES, CA | MC, TCA | 119.7 | 1755.3 |  |  |  |  |
| NEI20357 | 34.08696 | -118.0512 | BEAGLE MFG CO INC | EL MONTE, CA | MC | 128.8 |  |  |  |  |  |
| NEI20365 | 34.02684 | -117.9799 | BENTLEY MILLS INC | INDUSTRY, CA | TCA |  | 270.3 |  |  |  |  |
| NEI20366 | 33.99433 | -117.905 | BESTEEL | INDUSTRY, CA | TCA |  | 6254.0 |  |  |  |  |
| NEI20370 | 33.85998 | -118.1011 | BLAIR'S METAL POLISHING | CERRITOS, CA | TCA |  | 15739.2 |  |  |  |  |
| NEI20372 | 34.18993 | -118.3811 | BOBRICK WASHROOM EQUIP INC | NORTH HOLLYWOOD, CA | MC, TCA, PCE | 42.7 | 478.3 | 85.3 |  |  |  |
| NEI20389 | 34.0928 | -117.8811 | BROWN INTL CORP | COVINA, CA | TCA |  | 263.1 |  |  |  |  |
| NEI20390 | 33.93347 | -118.0721 | BRUNO'S ELECTRIC MOTOR REPAIR | SANTA FE SPRINGS, CA | PCE |  |  | 249.5 |  |  |  |
| NEI20396 | 34.16997 | -118.301 | BURBANK STEEL TREATING INC | BURBANK, CA | TCA |  | 4803.5 |  |  |  |  |
| NEI20398 | 34.28695 | -118.4285 | BURR MASTER INC | SAN FERNANDO, CA | TCA |  | 334.4 |  |  |  |  |
| NEI20411 | 34.06 | -118.1611 | CAL ST UNIV LA | LOS ANGELES, CA | TCE |  |  |  | 108.9 |  |  |
| NEI20415 | 34.03994 | -117.7911 | CAL ST, POLYTECHNIC UNIV, POMO | POMONA, CA | TCE |  |  |  | 128.8 |  |  |
| NEI20420 | 33.96605 | -118.0595 | CAL-TRON PLATING INC | SANTA FE SPRINGS, CA | TCA |  | 13607.8 |  |  |  |  |
| NEI20456 | 33.9599 | -118.3711 | CHARLES CAINE CO INC | LOS ANGELES, CA | TCA |  | 2239.2 |  |  |  |  |
| NEI20480 | 34.04066 | -118.3583 | COAST COIL CO | LOS ANGELES, CA | TCA |  | 1370.9 |  |  |  |  |
| NEI20484 | 33.86833 | -118.1923 | COAST METAL CRAFT CORP | RANCHO DOMINGUEZ, CA | TCA |  | 4385.8 |  |  |  |  |
| NEI20491 | 34.26997 | -118.4311 | COLOR-TEC INDUSTRIAL FINISHING | PACOIMA, CA | TCA |  | 2068.4 |  |  |  |  |
| NEI20497 | 34.14327 | -117.9885 | COMPOSITE STRUCTURES LLC | MONROVIA, CA | TCA |  | 70.0 |  |  |  |  |
| NEI20502 | 33.91053 | -118.3833 | CONSOL CONTROLS CORP PLT NO. 4 | EL SEGUNDO, CA | TCA |  | 761.1 |  |  |  |  |
| NEI20503 | 34.20995 | -118.4511 | CONSOL FABRICATORS CORP | SUN VALLEY, CA | TCA |  | 614.6 |  |  |  |  |
| NEI20508 | 34.07992 | -118.3311 | CONSOLIDATED FILM INDUSTRIES | HOLLYWOOD, CA | TCA, PCE |  | 90032.6 | 5297.9 |  |  |  |
| NEI20511 | 33.93995 | -118.4211 | CONTINENTAL AIRLINES INC (NSR | LOS ANGELES, CA | MC, TCA | 12854.0 | 3649.0 |  |  |  |  |
| NEI20517 | 33.87992 | -118.261 | CORONET MFG CO INC | GARDENA, CA | PCE |  |  | 3653.2 |  |  |  |
| NEI20521 | 33.83995 | -118.331 | COSMODYNE CORP | TORRANCE, CA | TCA |  | 2109.2 |  |  |  |  |
| NEI20528 | 34.04725 | -118.0551 | CRANEVEYOR CORP | SOUTH EL MONTE, CA | TCA |  | 2993.7 |  |  |  |  |
| NEI20538 | 34.24253 | -118.5939 | CUSTOM CONTROL SENSORS INC | CHATSWORTH, CA | TCA, PCE |  | 1621.1 | 330.7 |  |  |  |
| NEI20543 | 33.82721 | -118.3333 | CV INTL INC | TORRANCE, CA | TCA |  | 573.8 |  |  |  |  |
| NEI20551 | 33.85357 | -118.2267 | DAICO IND INC | COMPTON, CA | TCA |  | 1068.4 |  |  |  |  |
| NEI20553 | 33.99698 | -117.9126 | DARNELL CORP | INDUSTRY, CA | MC, TCA | 217.3 | 309.5 |  |  |  |  |
| NEI20555 | 34.09998 | -118.0037 | DATABYTE TECHNOLOGY INC | ARCADIA, CA | TCA |  | 382.1 |  |  |  |  |
| NEI20559 | 34.15164 | -118.0802 | DATATAPE INC | PASADENA, CA | TCA |  | 2281.6 |  |  |  |  |
| NEI20571 | 33.91494 | -118.3098 | DEL MAR DIE CASTING CO., INC | GARDENA, CA | TCE |  |  |  | 553.4 |  |  |
| NEI20572 | 33.93845 | -118.3859 | DELTA AIR LINES, INC | LOS ANGELES, CA | TCA |  | 326.0 |  |  |  |  |
| NEI20574 | 34.23808 | -118.5895 | DELUXE CORP | CHATSWORTH, CA | TCA |  | 9371.1 |  |  |  |  |
| NEI20575 | 34.08998 | -118.3011 | DELUXE LABORATORIES INC,DELUXE | HOLLYWOOD, CA | TCA |  | 196655.4 |  |  |  |  |
| NEI20579 | 33.89991 | -118.281 | DEUTSCH CO, METAL COMPONENTS D | GARDENA, CA | TCA |  | 16335.8 |  |  |  |  |
| NEI20583 | 34.02448 | -117.9725 | DEXTER CORP, ELECTRONIC MATERI | INDUSTRY, CA | TCA |  | 349.3 |  |  |  |  |
| NEI20588 | 33.89991 | -118.281 | DIE CAST PROD. INC | GARDENA, CA | PCE |  |  | 1091.3 |  |  |  |
| NEI20593 | 34.23377 | -118.5742 | DOOLING BROS INC | CHATSWORTH, CA | TCA |  | 1275.5 |  |  |  |  |
| NEI20594 | 34.00051 | -118.1389 | DORFILE COMPANY | COMMERCE, CA | TCA |  | 9836.1 |  |  |  |  |
| NEI20600 | 33.89582 | -118.0456 | DRAGON VALVE CO INC | NORWALK, CA | MC, TCA, TCE | 612.8 | 1021.5 |  | 50.3 |  |  |
| NEI20606 | 33.84813 | -118.2299 | E J S LIGHTING CORP | COMPTON, CA | PCE |  |  | 9871.1 |  |  |  |
| NEI20615 | 33.89991 | -118.3811 | EATON CORPORATION | EL SEGUNDO, CA | MC | 262.2 |  |  |  |  |  |
| NEI20617 | 34.09616 | -118.0297 | EDMONDSON ENTER. INC | TEMPLE CITY, CA | MC, TCA, PCE | 292.1 | 13723.4 | 365.1 |  |  |  |
| NEI20618 | 34.13998 | -118.2711 | EEMCO, DATRON INC DIV | LOS ANGELES, CA | MC, TCA, PCE | 426.0 | 1886.0 | 1289.8 |  |  |  |
| NEI20619 | 34.03997 | -118.031 | EEMUS MFG CORP | SOUTH EL MONTE, CA | TCA |  | 1055.1 |  |  |  |  |
| NEI20620 | 34.08999 | -117.871 | EG & G POWER SYSTEMS | COVINA, CA | TCA |  | 4483.1 |  |  |  |  |
| NEI20623 | 33.91741 | -118.0513 | ELECTRO-MAG | WHITTIER, CA | TCA |  | 743.3 |  |  |  |  |
| NEI20627 | 33.90999 | -118.3911 | ELECTROPLY INC | EL SEGUNDO, CA | TCA |  | 11283.1 |  |  |  |  |
| NEI20628 | 33.85994 | -118.211 | ELLIOTT'S DESIGNS INC | RANCHO DOMINGUEZ, CA | TCA |  | 14719.1 |  |  |  |  |
| NEI20639 | 33.82364 | -118.33 | EXCELLON AUTOMATION | TORRANCE, CA | TCA |  | 6559.4 |  |  |  |  |
| NEI20644 | 34.19026 | -118.5918 | FABER ENTER. INC | CANOGA PARK, CA | TCA |  | 5951.2 |  |  |  |  |
| NEI20663 | 34.05157 | -118.2664 | FIRST INTERSTATE BANK OF CALIF | LOS ANGELES, CA | TCA |  | 41.6 |  |  |  |  |
| NEI20675 | 34.11999 | -118.251 | FOREST LAWN MEM PARK ASSOC | GLENDALE, CA | MC, TCA | 44.9 | 394.2 |  |  |  |  |
| NEI20677 | 34.1694 | -118.2953 | FORTNER ENGINEERING & MFG INC | GLENDALE, CA | TCA |  | 525.9 |  |  |  |  |
| NEI20679 | 34.14999 | -118.3311 | FOTO-KEM /FOTO TRONICS | BURBANK, CA | TCA |  | 12575.8 |  |  |  |  |
| NEI20681 | 34.20578 | -118.3501 | FOUR MEDIA LABORATORY | BURBANK, CA | TCA |  | 7024.2 |  |  |  |  |
| NEI20685 | 33.87998 | -118.041 | FREDRICK RAMOND, INC | CERRITOS, CA | TCA |  | 7576.4 |  |  |  |  |
| NEI20687 | 33.8725 | -118.3146 | FREEMAN PRODUCTS, DIV AVNET, I | TORRANCE, CA | TCA |  | 9505.0 |  |  |  |  |
| NEI20688 | 33.99766 | -117.8932 | FREEMARC DESIGNS | INDUSTRY, CA | TCA |  | 150.2 |  |  |  |  |
| NEI20695 | 33.80921 | -118.3298 | GAMMA-F CORP | TORRANCE, CA | TCA |  | 12918.3 |  |  |  |  |
| NEI20698 | 34.09296 | -117.7196 | GARNER GLASS CO | CLAREMONT, CA | TCE |  |  |  | 709.9 |  |  |
| NEI20700 | 33.8675 | -118.2756 | GASKET MFG CO INC | GARDENA, CA | TCA |  | 3262.7 |  |  |  |  |
| NEI20725 | 34.00993 | -118.191 | GRANA INDUSTRIAL FINISHERS | LOS ANGELES, CA | TCA |  | 3284.5 |  |  |  |  |
| NEI20728 | 34.21997 | -118.3711 | GRAPHIC FINISHES INC | SUN VALLEY, CA | TCA |  | 3978.0 |  |  |  |  |
| NEI20746 | 33.98998 | -118.2211 | H & H ENAMELING INC | HUNTINGTON PARK, CA | TCA |  | 2581.4 |  |  |  |  |
| NEI20749 | 33.80993 | -118.1411 | HAGELIN AIRCRAFT MOTORS CO INC | LONG BEACH, CA | MC, TCA | 374.7 | 263.1 |  |  |  |  |
| NEI20756 | 34.20116 | -118.377 | HAWKER PACIFIC INC | SUN VALLEY, CA | TCA |  | 6162.5 |  |  |  |  |
| NEI20758 | 34.04998 | -117.801 | HAYWARD POOL PRODUCTS INC | POMONA, CA | MC, TCA | 13063.5 | 114.6 |  |  |  |  |
| NEI20768 | 34.04997 | -118.1911 | HIGHLAND AUTO & TRUCK SUPPLY | LOS ANGELES, CA | TCA |  | 968.4 |  |  |  |  |
| NEI20770 | 33.8886 | -118.0455 | HILLERICH & BRADSBY COMPANY, I | SANTA FE SPRINGS, CA | TCA |  | 7039.8 |  |  |  |  |
| NEI20776 | 34.04999 | -118.0611 | HOOTER BROS ENAMELING INC | SOUTH EL MONTE, CA | TCA |  | 1906.9 |  |  |  |  |
| NEI20777 | 34.04994 | -117.9911 | HOUSE OF PACKAGING, INC | INDUSTRY, CA | TCA |  | 22143.4 |  |  |  |  |
| NEI20781 | 33.81993 | -118.151 | HUCK INTERNATIONAL - DEUTSCH O | LAKEWOOD, CA | TCA |  | 20458.4 |  |  |  |  |
| NEI20787 | 33.91586 | -118.3899 | HUGHES AIRCRAFT CO, EDSG | EL SEGUNDO, CA | MC, TCA | 32.1 | 11234.8 |  |  |  |  |
| NEI20792 | 33.81991 | -118.201 | HUGHES TECHNICAL SERVICES COMP | LONG BEACH, CA | TCA |  | 425.0 |  |  |  |  |
| NEI20794 | 33.7561 | -118.2514 | HUGO NEU-PROLER CO | TERMINAL ISLAND, CA | TCA |  | 503.5 |  |  |  |  |
| NEI20801 | 33.99889 | -117.8985 | HYDRO TECH CHEM CORP | INDUSTRY, CA | TCA |  | 18332.4 |  |  |  |  |
| NEI20807 | 33.90997 | -118.241 | IDEAL METAL PROCESSING CO | COMPTON, CA | TCA |  | 9684.6 |  |  |  |  |
| NEI20809 | 33.89677 | -118.0391 | IMB ELECTRONIC PRODUCTS INC | SANTA FE SPRINGS, CA | TCA |  | 2526.3 |  |  |  |  |
| NEI20815 | 34.21083 | -118.4598 | INDUSTRIAL ELECTRONIC ENGINEER | VAN NUYS, CA | TCA |  | 1740.8 |  |  |  |  |
| NEI20820 | 33.97999 | -118.201 | INDUSTRIAL STEEL TREATING CO, | HUNTINGTON PARK, CA | TCA |  | 45012.2 |  |  |  |  |
| NEI20827 | 33.91936 | -118.3996 | INTL RECTIFIER CORP | EL SEGUNDO, CA | TCA, PCE |  | 45.1 | 1545.4 |  |  |  |
| NEI20829 | 33.98517 | -118.4018 | INTERNATIONL AUTO BODY | CULVER CITY, CA | TCA |  | 425.1 |  |  |  |  |
| NEI20836 | 34.01725 | -117.9745 | ITT BARTON | INDUSTRY, CA | TCA |  | 2942.5 |  |  |  |  |
| NEI20840 | 33.96 | -118.141 | J. P. TURGEON & SONS INC | BELL GARDENS, CA | TCA |  | 22268.2 |  |  |  |  |
| NEI20844 | 34.19929 | -118.3446 | JANCO CORP | BURBANK, CA | TCA |  | 2224.9 |  |  |  |  |
| NEI20845 | 34.22334 | -118.5027 | JBL INC | NORTHRIDGE, CA | TCA |  | 6167.7 |  |  |  |  |
| NEI20860 | 34.0002 | -118.0729 | KATER-CRAFTS BOOKBINDERS | PICO RIVERA, CA | TCE |  |  |  | 314.3 |  |  |
| NEI20861 | 33.90993 | -118.0511 | KEENE CORP, REINHOLD INDUSTRIE | SANTA FE SPRINGS, CA | MC, TCA | 4309.1 | 222.3 |  |  |  |  |
| NEI20865 | 34.03094 | -118.2552 | KEYSTONE ENGINEERING CO | LOS ANGELES, CA | TCA |  | 210.3 |  |  |  |  |
| NEI20877 | 33.99876 | -118.2266 | L & F IND | HUNTINGTON PARK, CA | TCA |  | 272.6 |  |  |  |  |
| NEI20890 | 33.92441 | -118.4311 | LA CITY, SANITATION BUREAU (NS | PLAYA DEL REY, CA | MC, TCA | 9.5 | 66.7 |  |  |  |  |
| NEI20904 | 34.03832 | -118.2391 | LA CO., METROPOLITAN TRANS AUT | LOS ANGELES, CA | MC, TCA | 32.2 | 432.3 |  |  |  |  |
| NEI20918 | 33.82172 | -118.3408 | LA GARD INC | TORRANCE, CA | TCA |  | 145.5 |  |  |  |  |
| NEI20919 | 34.20758 | -118.3501 | THE TRIUMPH OPERATING GRP INC, | SUN VALLEY, CA | TCA |  | 855.9 |  |  |  |  |
| NEI20926 | 33.77477 | -118.2601 | LAIDLAW ENVIRONMENTAL SERVICES | WILMINGTON, CA | MC, TCA, PCE | 28.5 | 25.0 | 0.3 |  |  |  |
| NEI20929 | 34.0129 | -117.9539 | LANSCO DIE CASTING INC/INDUSTR | INDUSTRY, CA | TCA |  | 10285.7 |  |  |  |  |
| NEI20930 | 34.05189 | -118.0389 | LAWSON HUGHES CO., INC | SOUTH EL MONTE, CA | TCA |  | 3603.4 |  |  |  |  |
| NEI20940 | 34.01596 | -117.8371 | LIBBEY GLASS INC | INDUSTRY, CA | MC | 34.3 |  |  |  |  |  |
| NEI20942 | 33.87699 | -118.2292 | LIGHTOLIER INC | COMPTON, CA | MC, TCA | 2497.9 | 10657.2 |  |  |  |  |
| NEI20950 | 33.88991 | -118.1711 | LOCKHART IND INC | PARAMOUNT, CA | PCE |  |  | 5102.0 |  |  |  |
| NEI20955 | 33.77998 | -118.1611 | LONG BEACH PUBLIC TRANPORTATIO | LONG BEACH, CA | MC, TCA | 19.4 | 2.3 |  |  |  |  |
| NEI20959 | 34.15165 | -118.0791 | LORAL ELECTRO-OPTICAL SYSTEMS | PASADENA, CA | TCA |  | 1555.8 |  |  |  |  |
| NEI20975 | 34.22994 | -118.5911 | MACCAULEY INSTRUMENTS CORP | CHATSWORTH, CA | TCA |  | 2947.4 |  |  |  |  |
| NEI20982 | 33.83889 | -118.3367 | MAGNAVOX ELECTRONIC SYSTEMS CO | TORRANCE, CA | TCA, PCE |  | 3996.2 | 314.8 |  |  |  |
| NEI20989 | 34.07832 | -117.8896 | MARLEE MANUFACTURING, INC. | COVINA, CA | TCA |  | 764.8 |  |  |  |  |
| NEI20998 | 34.24996 | -118.3911 | MAYONI ENTERPRISES | PACOIMA, CA | TCA |  | 5430.0 |  |  |  |  |
| NEI21002 | 34.13993 | -117.981 | MCDONNELL DOUGLAS AEROSPACE | MONROVIA, CA | TCA |  | 5156.0 |  |  |  |  |
| NEI21005 | 33.88992 | -118.271 | MECH METAL FINISHING CO | GARDENA, CA | TCA |  | 14549.0 |  |  |  |  |
| NEI21008 | 34.21611 | -118.4707 | MEGA SOUND INC,MAGNETIC PRODUC | VAN NUYS, CA | TCA |  | 232.0 |  |  |  |  |
| NEI21011 | 34.17651 | -118.3083 | MENASCO MFG CO (EIS USE) | BURBANK, CA | TCA |  | 36737.8 |  |  |  |  |
| NEI21017 | 33.81544 | -118.251 | METAL CONTAINER CORP OF CALIFO | CARSON, CA | TCA |  | 9.1 |  |  |  |  |
| NEI21018 | 33.94998 | -118.151 | METAL SURFACES INC | BELL GARDENS, CA | TCA, PCE |  | 14636.5 | 1602.1 |  |  |  |
| NEI21019 | 34.13425 | -118.003 | METRIC MACHINING | MONROVIA, CA | PCE |  |  | 327.0 |  |  |  |
| NEI21020 | 33.77574 | -118.2537 | METROPOLITAN STEVEDORE CO | WILMINGTON, CA | TCA, PCE |  | 143.5 | 49.1 |  |  |  |
| NEI21030 | 34.1694 | -118.2953 | MINARIK ELECTRIC CO. | GLENDALE, CA | TCA |  | 235.9 |  |  |  |  |
| NEI21044 | 34.02126 | -118.2313 | MONICO ALLOYS, INC | LOS ANGELES, CA | TCA |  | 3556.6 |  |  |  |  |
| NEI21045 | 33.98426 | -118.1409 | MONOGRAM AEROSPACE FASTENERS, | LOS ANGELES, CA | TCA |  | 233.1 |  |  |  |  |
| NEI21046 | 33.92595 | -118.1066 | MONOGRAM IND, PEACOCK ENGINEER | NORWALK, CA | TCA |  | 6891.9 |  |  |  |  |
| NEI21050 | 34.00392 | -118.1596 | MOTO-PARTS EXCHANGE CO INC | COMMERCE, CA | TCA |  | 3257.7 |  |  |  |  |
| NEI21058 | 33.83999 | -118.2319 | NALCO CHEMICAL CO | CARSON, CA | MC | 10.0 |  |  |  |  |  |
| NEI21059 | 34.18995 | -118.171 | NASA JET PROPULSION LAB | PASADENA, CA | TCA |  | 906.3 |  |  |  |  |
| NEI21066 | 33.93997 | -118.3711 | NATL TECH SYS | LOS ANGELES, CA | TCA |  | 6466.8 |  |  |  |  |
| NEI21068 | 34.07992 | -118.0411 | NAVCOM DEFENSE ELECTRONICS INC | EL MONTE, CA | MC, TCA | 3816.5 | 3429.2 |  |  |  |  |
| NEI21071 | 34.2599 | -118.5758 | NETWORKS ELECTRONIC CORP | CHATSWORTH, CA | MC, TCA | 35.5 | 7584.1 |  |  |  |  |
| NEI21072 | 33.92995 | -118.051 | NEWMARK PROD. INC | SANTA FE SPRINGS, CA | TCA |  | 2199.5 |  |  |  |  |
| NEI21086 | 33.91998 | -118.3111 | NORTHROP GRUMMAN CO, ELECTRONI | HAWTHORNE, CA | TCA |  | 171.6 |  |  |  |  |
| NEI21090 | 34.23995 | -118.391 | NUPLA CORP | SUN VALLEY, CA | MC | 544.3 |  |  |  |  |  |
| NEI21097 | 34.20237 | -118.413 | ONTIC ENGINEERING & MANUFACTUR | NORTH HOLLYWOOD, CA | TCA |  | 143.8 |  |  |  |  |
| NEI21099 | 33.88991 | -118.0511 | ORANGE CO. NAME PLATE CO INC | SANTA FE SPRINGS, CA | TCA |  | 2382.5 |  |  |  |  |
| NEI21100 | 33.87249 | -118.0313 | ORBIT TESTING INC | CERRITOS, CA | TCA |  | 1564.9 |  |  |  |  |
| NEI21101 | 34.17908 | -118.3171 | OROAMERICA | BURBANK, CA | TCA |  | 192.4 |  |  |  |  |
| NEI21104 | 33.98822 | -118.2101 | OWENS-BROCKWAY GLASS CONTAINER | VERNON, CA | TCA |  | 7809.6 |  |  |  |  |
| NEI21108 | 33.91264 | -118.3066 | P.B. FASTENERS | GARDENA, CA | PCE |  |  | 0.2 |  |  |  |
| NEI21110 | 34.20129 | -118.3479 | PACIFIC AIRMOTIVE CORP | BURBANK, CA | TCA |  | 8850.8 |  |  |  |  |
| NEI21139 | 33.99868 | -118.1411 | PAULY INC | COMMERCE, CA | TCA |  | 2124.6 |  |  |  |  |
| NEI21140 | 34.23123 | -118.4884 | PCA ELECTRONICS INC | SEPULVEDA, CA | TCA |  | 2698.9 |  |  |  |  |
| NEI21146 | 33.87999 | -118.2711 | PERMALITE REPROMEDIA CORP | GARDENA, CA | TCA |  | 277.1 |  |  |  |  |
| NEI21153 | 34.12994 | -117.9211 | PHAOSTRON INSTRUMENT & ELECTRO | AZUSA, CA | PCE |  |  | 61.2 |  |  |  |
| NEI21158 | 34.07999 | -118.341 | PHYLRICH INTERNATIONAL | LOS ANGELES, CA | TCA |  | 3547.5 |  |  |  |  |
| NEI21165 | 34.04824 | -118.035 | PLASTIC DRESS-UP CO | SOUTH EL MONTE, CA | TCA |  | 6833.4 |  |  |  |  |
| NEI21168 | 33.99889 | -117.8985 | PLATO PROD INC | INDUSTRY, CA | PCE |  |  | 514.4 |  |  |  |
| NEI21178 | 33.78994 | -118.2311 | PRAXAIR INC | WILMINGTON, CA | TCA |  | 35.2 |  |  |  |  |
| NEI21181 | 33.89 | -118.041 | PRECISION TUBE BENDING | SANTA FE SPRINGS, CA | PCE |  |  | 92.1 |  |  |  |
| NEI21182 | 33.89207 | -118.1624 | PREMIUM PLASTICS INC | PARAMOUNT, CA | TCA |  | 2380.0 |  |  |  |  |
| NEI21193 | 34.22339 | -118.3884 | PYRAMID POWDER COATING | SUN VALLEY, CA | TCA |  | 1382.5 |  |  |  |  |
| NEI21197 | 34.24996 | -118.3911 | QUALITY FINISHING INC | SUN VALLEY, CA | TCA |  | 3102.6 |  |  |  |  |
| NEI21198 | 33.91753 | -118.3206 | QUALITY HARDWARE MFG CO INC | HAWTHORNE, CA | TCA |  | 6361.6 |  |  |  |  |
| NEI21203 | 34.19462 | -118.3803 | R & B AIRCRAFT SUPPLY INC | NORTH HOLLYWOOD, CA | TCA |  | 383.2 |  |  |  |  |
| NEI21204 | 34.05993 | -117.971 | R & G ENAMELING | BALDWIN PARK, CA | TCA |  | 12464.7 |  |  |  |  |
| NEI21209 | 34.19985 | -118.3967 | RAINTREE BUCKLES & JEWELRY INC | NORTH HOLLYWOOD, CA | TCA |  | 4556.8 |  |  |  |  |
| NEI21216 | 33.98812 | -118.2968 | RAPID INDUSTRIES | LOS ANGELES, CA | TCA |  | 124.7 |  |  |  |  |
| NEI21219 | 33.96999 | -118.041 | RASMUSSEN IRON WORKS INC | WHITTIER, CA | TCA |  | 1362.1 |  |  |  |  |
| NEI21224 | 33.97996 | -118.1181 | RELIABLE METALLURGICAL PROCESS | MONTEBELLO, CA | TCA |  | 141.0 |  |  |  |  |
| NEI21226 | 34.20328 | -118.4119 | REMO INC | NORTH HOLLYWOOD, CA | MC, TCA | 758.6 | 1132.8 |  |  |  |  |
| NEI21228 | 33.8725 | -118.0302 | REVERE TRANSDUCERS INC | CERRITOS, CA | TCA |  | 2809.6 |  |  |  |  |
| NEI21235 | 34.04994 | -117.9911 | ROBERT H. PETERSON CO | INDUSTRY, CA | MC | 300.1 |  |  |  |  |  |
| NEI21236 | 33.99635 | -118.2861 | ROBERT M. HADLEY CO INC | LOS ANGELES, CA | MC, TCA, PCE | 241.6 | 353.3 | 95.7 |  |  |  |
| NEI21238 | 33.80021 | -118.3286 | ROBINSON HELICOPTER CO INC | TORRANCE, CA | TCA |  | 4556.3 |  |  |  |  |
| NEI21249 | 34.0167 | -118.0417 | ROSE HILLS MEM PARK ASSOC | WHITTIER, CA | PCE |  |  | 10.8 |  |  |  |
| NEI21250 | 34.01999 | -118.241 | ROY E. HANSON JR MFG CO | LOS ANGELES, CA | TCA |  | 19958.1 |  |  |  |  |
| NEI21255 | 34.13311 | -117.9195 | RUBBER/URETHANES INCORPORATED | AZUSA, CA | PCE |  |  | 1753.1 |  |  |  |
| NEI21267 | 33.87998 | -118.281 | SANI-TOP INC | GARDENA, CA | TCA, PCE |  | 412.3 | 694.4 |  |  |  |
| NEI21276 | 34.04999 | -118.0511 | SEACHROME CORP | SOUTH EL MONTE, CA | TCA |  | 4136.8 |  |  |  |  |
| NEI21281 | 34.02607 | -118.3732 | SEE'S CANDY SHOPS INC | LOS ANGELES, CA | PCE |  |  | 121.0 |  |  |  |
| NEI21282 | 34.2017 | -118.3426 | SENIOR FLEXONICS INC/STAINLESS STEEL DVN | BURBANK, CA | PCE |  |  | 5599.8 |  |  |  |
| NEI21295 | 33.8455 | -118.3098 | SHINTOM WEST CORP OF AMERICA | TORRANCE, CA | TCA |  | 219.1 |  |  |  |  |
| NEI21304 | 34.05833 | -117.7778 | SIMPSON PAPER CO @ COGEN UNIT | POMONA, CA | TCA |  | 3262.7 |  |  |  |  |
| NEI21325 | 34.12364 | -117.9779 | SOUTHWEST PRODUCTS CO | IRWINDALE, CA | TCA |  | 1167.7 |  |  |  |  |
| NEI21332 | 33.92018 | -118.4072 | SPECTRUM METAL FINISHERS INC | EL SEGUNDO, CA | TCA |  | 1433.9 |  |  |  |  |
| NEI21339 | 33.97404 | -118.2488 | STANDARD NICKEL CHROMIUM PLATING CO INC | LOS ANGELES, CA | PCE |  |  | 20164.9 |  |  |  |
| NEI21349 | 33.99995 | -118.1211 | STONE CONTAINER CORP | LOS ANGELES, CA | MC, PCE | 244.0 |  | 202.3 |  |  |  |
| NEI21350 | 33.89997 | -118.301 | STONE MFG CO | GARDENA, CA | MC, PCE, TCE | 458.1 |  | 322.5 | 68.5 |  |  |
| NEI21359 | 34.10224 | -117.8205 | SUN BADGE CO | SAN DIMAS, CA | TCA |  | 956.6 |  |  |  |  |
| NEI21365 | 34.01998 | -117.971 | SUNSET FIREPLACE FIXTURES INC | INDUSTRY, CA | PCE |  |  | 5864.9 |  |  |  |
| NEI21368 | 34.19682 | -118.3445 | SURFACE FINISHING INC | BURBANK, CA | TCA |  | 10623.6 |  |  |  |  |
| NEI21373 | 33.89812 | -118.2793 | T&V INDUSTRIES | GARDENA, CA | TCA |  | 667.5 |  |  |  |  |
| NEI21378 | 34.13992 | -118.3611 | TECHNICOLOR INC | NORTH HOLLYWOOD, CA | TCA, PCE |  | 30023.7 | 8651.8 |  |  |  |
| NEI21381 | 34 | -117.931 | TELEDYNE CAST PARTS-INDUSTRY O | INDUSTRY, CA | TCA |  | 821.0 |  |  |  |  |
| NEI21382 | 34.03232 | -118.4567 | TELEDYNE CONTROLS, DIV TELEDYN | LOS ANGELES, CA | TCA |  | 4343.6 |  |  |  |  |
| NEI21383 | 34.23575 | -118.5601 | TELEDYNE ELECTRONIC SYSTEMS | NORTHRIDGE, CA | TCA |  | 438.2 |  |  |  |  |
| NEI21384 | 33.90997 | -118.311 | TELEDYNE IND.INC, TELEDYNE REL | HAWTHORNE, CA | TCA |  | 5395.0 |  |  |  |  |
| NEI21385 | 33.98305 | -118.4288 | TELEDYNE MICROELECTRONICS UNIT | LOS ANGELES, CA | TCA |  | 3065.0 |  |  |  |  |
| NEI21406 | 33.91713 | -118.1822 | THE GADGET MFG CO | LYNWOOD, CA | TCA |  | 272.2 |  |  |  |  |
| NEI21407 | 34.01992 | -118.4611 | THE GILLETTE CO, PAPER MATE GR | SANTA MONICA, CA | TCA, PCE |  | 509.4 | 2090.2 |  |  |  |
| NEI21431 | 33.92537 | -118.1693 | TITAN IND | SOUTH GATE, CA | TCA |  | 1796.2 |  |  |  |  |
| NEI21436 | 33.84422 | -118.3444 | TORRANCE CITY | TORRANCE, CA | MC, TCA, PCE | 28.2 | 73.1 | 26.4 |  |  |  |
| NEI21439 | 33.93997 | -118.411 | TRANS WORLD AIRLINES INC | LOS ANGELES, CA | MC, TCA | 1.8 | 6.4 |  |  |  |  |
| NEI21440 | 33.97769 | -118.4244 | TRANSACTION TECH INC | LOS ANGELES, CA | TCA |  | 1243.6 |  |  |  |  |
| NEI21441 | 34.01199 | -118.1651 | TRANSDIGM INC, ADEL WIGGINS GR | LOS ANGELES, CA | TCA |  | 2485.7 |  |  |  |  |
| NEI21444 | 34.01434 | -118.2019 | TRIANGLE BRASS MFG CO | LOS ANGELES, CA | TCA |  | 6319.0 |  |  |  |  |
| NEI21445 | 33.98898 | -118.2135 | TRICO INDUSTRIES INC. | HUNTINGTON PARK, CA | MC, TCA | 1637.9 | 12360.6 |  |  |  |  |
| NEI21447 | 33.89475 | -118.1646 | TRIPROCESS CO INC | PARAMOUNT, CA | TCA |  | 115.5 |  |  |  |  |
| NEI21449 | 33.98217 | -118.2621 | TROJAN METAL PROD. | LOS ANGELES, CA | TCA |  | 2810.5 |  |  |  |  |
| NEI21450 | 34.10999 | -118.241 | TRU CUT INC | LOS ANGELES, CA | PCE |  |  | 886.7 |  |  |  |
| NEI21452 | 33.87991 | -118.3711 | TRW INC, (EIS & NSR USE ONLY) | MANHATTAN BEACH, CA | MC, TCE | 18.1 |  |  | 204.1 |  |  |
| NEI21463 | 34.0132 | -117.9149 | U S TSUBAKI INC | INDUSTRY, CA | TCA, PCE |  | 0.1 | 0.1 |  |  |  |
| NEI21478 | 34.20347 | -118.3956 | UNITED AERONAUTICAL CORP | NORTH HOLLYWOOD, CA | MC | 469.6 |  |  |  |  |  |
| NEI21488 | 34.13824 | -118.3618 | UNIVERSAL STUDIOS INC (EIS USE | UNIVERSAL CITY, CA | TCA |  | 49.5 |  |  |  |  |
| NEI21499 | 33.74866 | -118.2453 | US GOVT, NAVY DEPT LB SHIPYARD | LONG BEACH, CA | TCA, PCE |  | 6448.7 | 80.7 |  |  |  |
| NEI21507 | 34.03997 | -118.041 | VACCO INDUSTRIES | SOUTH EL MONTE, CA | TCA |  | 2978.7 |  |  |  |  |
| NEI21508 | 34.22693 | -118.5448 | VALIDYNE ENGINEERING CORP | NORTHRIDGE, CA | TCA |  | 472.7 |  |  |  |  |
| NEI21516 | 33.79997 | -118.2911 | VARIAN SAMPLE PREPARATION PROD | HARBOR CITY, CA | MC | 3849.2 |  |  |  |  |  |
| NEI21518 | 34.10409 | -117.814 | VEMCO CORP | SAN DIMAS, CA | TCA |  | 6318.1 |  |  |  |  |
| NEI21526 | 34.15954 | -118.2897 | W & F MFG INC | GLENDALE, CA | TCA |  | 1799.0 |  |  |  |  |
| NEI21531 | 33.89269 | -118.2813 | WALTCO ENGINEERING CO | GARDENA, CA | TCA |  | 97622.1 |  |  |  |  |
| NEI21544 | 34.27612 | -118.4294 | WELCH METAL PROD. INC | SAN FERNANDO, CA | MC, TCA | 400.5 | 1525.8 |  |  |  |  |
| NEI21565 | 34.19995 | -118.4111 | WHITTAKER CONTROLS INC | NORTH HOLLYWOOD, CA | TCA |  | 5504.8 |  |  |  |  |
| NEI21573 | 34.00374 | -118.1289 | GRAPHIC PRESS, INC. | COMMERCE, CA | PCE |  |  | 32.0 |  |  |  |
| NEI21575 | 34.1041 | -118.2444 | WONTRONICS INC | LOS ANGELES, CA | TCA |  | 1007.0 |  |  |  |  |
| NEI21943 | 33.70997 | -117.841 | A. C. D. INC | SANTA ANA, CA | TCA |  | 11431.9 |  |  |  |  |
| NEI21958 | 33.85303 | -117.8635 | ALL-BANN ENTER. INC | ANAHEIM, CA | TCA |  | 5375.2 |  |  |  |  |
| NEI21961 | 33.85996 | -117.891 | AMERICAN ELECTRONICS INC | FULLERTON, CA | PCE |  |  | 1627.9 |  |  |  |
| NEI21976 | 33.70646 | -117.9289 | AST RESEARCH INC | FOUNTAIN VALLEY, CA | TCA |  | 2986.2 |  |  |  |  |
| NEI21981 | 33.69993 | -117.991 | B & B ENAMELING INC | HUNTINGTON BEACH, CA | TCA |  | 2591.4 |  |  |  |  |
| NEI21988 | 33.86208 | -117.8604 | BASF STRUCTURAL MATERIALS INC | ANAHEIM, CA | TCA |  | 572.9 |  |  |  |  |
| NEI21991 | 33.77714 | -118.001 | BAZZ-HOUSTON CO | GARDEN GROVE, CA | PCE |  |  | 11138.9 |  |  |  |
| NEI21992 | 33.92649 | -117.9324 | BECKMAN INSTRUMENTS INC (EIS & | FULLERTON, CA | TCA |  | 10728.8 |  |  |  |  |
| NEI21996 | 33.92477 | -117.9205 | BI TECHNOLOGIES, CORPORATION | FULLERTON, CA | TCA |  | 955.1 |  |  |  |  |
| NEI22010 | 33.8781 | -117.8897 | CALIFORNIA STATE UNIVERSITY, F | FULLERTON, CA | TCA, PCE |  | 0.1 | 0.1 |  |  |  |
| NEI22012 | 33.64922 | -117.7213 | CALSONIC CLIMATE CONTROL INC | IRVINE, CA | TCA |  | 5222.4 |  |  |  |  |
| NEI22014 | 33.67998 | -117.861 | CANON BUSINESS MACHINES INC | COSTA MESA, CA | TCA |  | 2491.6 |  |  |  |  |
| NEI22017 | 33.6699 | -117.871 | CERADYNE INC | COSTA MESA, CA | TCA |  | 2683.6 |  |  |  |  |
| NEI22022 | 33.85976 | -117.803 | HEXCEL CORPORATION | ANAHEIM, CA | TCA |  | 102.5 |  |  |  |  |
| NEI22029 | 33.86155 | -117.8041 | CONTROL DATA CORPORATION | ANAHEIM, CA | TCA |  | 836.0 |  |  |  |  |
| NEI22035 | 33.80991 | -117.8911 | CREST COATING INC | ANAHEIM, CA | TCA |  | 7363.6 |  |  |  |  |
| NEI22045 | 33.79993 | -117.861 | DESIGNS ALIVE INC | ORANGE, CA | TCA, PCE |  | 5.4 | 5.4 |  |  |  |
| NEI22048 | 33.63425 | -117.9357 | EATON CORPORATION, MSC PRODUCT | COSTA MESA, CA | MC, TCA | 25.4 | 3515.8 |  |  |  |  |
| NEI22049 | 33.84995 | -117.841 | ECONOLITE CONTROL PRODUCTS, IN | ANAHEIM, CA | TCA |  | 5195.9 |  |  |  |  |
| NEI22051 | 33.84995 | -117.841 | ELECTRO METAL FINISHING CORPOR | ANAHEIM, CA | TCA |  | 8794.7 |  |  |  |  |
| NEI22055 | 33.70517 | -117.8566 | ELPAC ELECTRONICS INC | SANTA ANA, CA | TCA |  | 2653.6 |  |  |  |  |
| NEI22058 | 33.68369 | -117.8327 | EVEREST, A DIVISION OF WRIGHT | ANAHEIM, CA | TCA |  | 1114.6 |  |  |  |  |
| NEI22060 | 33.7147 | -117.9118 | EXPRESS MFG INC | SANTA ANA, CA | TCA |  | 3251.8 |  |  |  |  |
| NEI22062 | 33.72011 | -117.9118 | FAIRCHILD FASTENER GROUP,ROSAN | SANTA ANA, CA | TCA |  | 2085.6 |  |  |  |  |
| NEI22065 | 33.70992 | -117.861 | FILTER CONCEPTS INC | SANTA ANA, CA | TCA |  | 1214.7 |  |  |  |  |
| NEI22066 | 33.71284 | -117.9193 | FIRE PLACE MFG INC | SANTA ANA, CA | TCA, PCE |  | 1052.9 | 0.6 |  |  |  |
| NEI22067 | 33.74221 | -117.9703 | FLETCHER ENGINEERING INC | WESTMINSTER, CA | PCE |  |  | 684.7 |  |  |  |
| NEI22074 | 33.85315 | -117.8473 | FURON CO | ANAHEIM, CA | TCA |  | 7239.3 |  |  |  |  |
| NEI22079 | 33.74037 | -117.8537 | GGC INC | SANTA ANA, CA | TCA |  | 1990.8 |  |  |  |  |
| NEI22087 | 33.62996 | -117.931 | GULTON STATHAM TRANSDUCERS | COSTA MESA, CA | TCA |  | 7671.2 |  |  |  |  |
| NEI22091 | 33.80676 | -117.9019 | HARDIN MARINE | ANAHEIM, CA | TCA |  | 956.6 |  |  |  |  |
| NEI22094 | 33.72594 | -117.8525 | HIGH-TECH COATINGS | SANTA ANA, CA | TCA |  | 1496.9 |  |  |  |  |
| NEI22099 | 33.62994 | -117.921 | HUGHES AIRCRAFT CO, MICROELECT | NEWPORT BEACH, CA | TCA |  | 1349.9 |  |  |  |  |
| NEI22106 | 33.82198 | -117.9183 | INTERSTATE ELECTRONICS CORP | ANAHEIM, CA | TCA |  | 967.5 |  |  |  |  |
| NEI22112 | 33.71991 | -117.8511 | J.L. WOOD OPTICAL SYS | SANTA ANA, CA | TCA |  | 1333.8 |  |  |  |  |
| NEI22117 | 33.85996 | -117.891 | JOHNSON CONTROLS BATTERY GROUP | FULLERTON, CA | MC, TCA | 640.0 | 634.6 |  |  |  |  |
| NEI22118 | 33.71273 | -117.9333 | KAGA INC | FOUNTAIN VALLEY, CA | TCA |  | 8064.4 |  |  |  |  |
| NEI22119 | 33.68997 | -117.851 | KAISER ELECTROPRECISION | IRVINE, CA | TCA |  | 26233.5 |  |  |  |  |
| NEI22124 | 33.8457 | -117.9985 | KNOTT'S BERRY FARM | BUENA PARK, CA | TCA, PCE |  | 4.5 | 4.5 |  |  |  |
| NEI22137 | 33.85882 | -117.8084 | LING ELECTRONICS INC, SUBS MEC | ANAHEIM, CA | MC | 642.3 |  |  |  |  |  |
| NEI22138 | 33.84942 | -117.8645 | LITE CTR OF CAL | ANAHEIM, CA | TCA |  | 30.6 |  |  |  |  |
| NEI22144 | 33.81851 | -117.8988 | POWER PARAGON INC | ANAHEIM, CA | TCA |  | 5554.5 |  |  |  |  |
| NEI22153 | 33.74451 | -118.0366 | MCDONNELL DOUGLAS CORP, SUB OF BOEING CO | HUNTINGTON BEACH, CA | MC, PCE, TCE | 58.2 |  | 21.2 | 630.0 |  |  |
| NEI22160 | 33.86276 | -117.8876 | FAIRCHILD HOLDING CORP, FAIRCHILD FASTEN | FULLERTON, CA | PCE |  |  | 64091.6 |  |  |  |
| NEI22162 | 33.70991 | -117.901 | MICROSEMI CORP | SANTA ANA, CA | TCA, PCE |  | 778.4 | 8634.1 |  |  |  |
| NEI22176 | 33.70823 | -117.9322 | NEWPORT ADHESIVE INC | FOUNTAIN VALLEY, CA | MC | 7620.4 |  |  |  |  |  |
| NEI22180 | 33.79606 | -118.0034 | OCA APPLIED OPTICS INC | GARDEN GROVE, CA | TCA |  | 1953.2 |  |  |  |  |
| NEI22181 | 33.7099 | -117.8511 | ONE WAY MFG | SANTA ANA, CA | TCA |  | 2199.5 |  |  |  |  |
| NEI22183 | 33.85996 | -117.891 | OR. CO. PAINTING | FULLERTON, CA | TCA |  | 7983.2 |  |  |  |  |
| NEI22191 | 33.68995 | -117.841 | PACKARD HUGHES INTERCONNECT | IRVINE, CA | TCA |  | 823.7 |  |  |  |  |
| NEI22192 | 33.67097 | -117.8476 | PARKER HANNIFIN AEROSPACE CORP | IRVINE, CA | PCE |  |  | 22588.9 |  |  |  |
| NEI22207 | 33.69542 | -117.8317 | PROGRAM DATA INC | IRVINE, CA | MC, TCA | 25.1 | 110.2 |  |  |  |  |
| NEI22209 | 33.69554 | -117.9407 | PSITECH | FOUNTAIN VALLEY, CA | TCA |  | 136.1 |  |  |  |  |
| NEI22210 | 33.70786 | -117.8599 | QED INC. | SANTA ANA, CA | TCA |  | 1337.2 |  |  |  |  |
| NEI22222 | 33.6699 | -117.871 | ROCKWELL INTERNATIONAL COLLINS | COSTA MESA, CA | TCA |  | 170.6 |  |  |  |  |
| NEI22239 | 33.68071 | -117.8726 | SEMICOA | COSTA MESA, CA | TCA |  | 224.5 |  |  |  |  |
| NEI22241 | 33.85995 | -117.801 | SETCO INC | ANAHEIM, CA | TCA |  | 1938.4 |  |  |  |  |
| NEI22253 | 33.73998 | -118.0011 | SO CAL EDISON CO (EIS USE) | WESTMINSTER, CA | TCA |  | 160.6 |  |  |  |  |
| NEI22254 | 33.86115 | -117.8636 | SONFARREL INC | ANAHEIM, CA | MC | 274.8 |  |  |  |  |  |
| NEI22255 | 33.69168 | -117.8511 | SORIN BIOMEDICAL INC | IRVINE, CA | MC, TCA | 283.0 | 1618.4 |  |  |  |  |
| NEI22259 | 33.71991 | -117.8511 | SPEEDWAY METAL FINISHING | SANTA ANA, CA | PCE |  |  | 214.2 |  |  |  |
| NEI22260 | 33.71284 | -117.9193 | SPS TECHNOLOGIES INC | SANTA ANA, CA | MC, TCA | 480.5 | 5488.5 |  |  |  |  |
| NEI22271 | 33.70748 | -117.9128 | SURVIVAIR, A DIV OF COMASEC IN | SANTA ANA, CA | TCA |  | 272.2 |  |  |  |  |
| NEI22277 | 33.80991 | -117.951 | TAYLOR-DUNN MFG CO | ANAHEIM, CA | TCA |  | 63.4 |  |  |  |  |
| NEI22280 | 33.55509 | -117.7754 | TELONIC BERKELEY INC | LAGUNA BEACH, CA | TCA |  | 490.3 |  |  |  |  |
| NEI22288 | 33.85991 | -117.821 | THE HARTWELL CORP | PLACENTIA, CA | TCA |  | 1882.4 |  |  |  |  |
| NEI22292 | 33.80994 | -117.861 | THERMCO SYSTEMS CORP | ORANGE, CA | TCA |  | 522.5 |  |  |  |  |
| NEI22295 | 33.7299 | -118.0311 | TIODIZE INC | HUNTINGTON BEACH, CA | PCE |  |  | 2222.6 |  |  |  |
| NEI22323 | 33.78994 | -117.8711 | VARCO INTL INC. | ORANGE, CA | MC, TCA, PCE | 14.5 | 804.7 | 3.2 |  |  |  |
| NEI22326 | 33.7999 | -118.051 | VESPER CORP | LOS ALAMITOS, CA | TCA, PCE |  | 731.8 | 5740.2 |  |  |  |
| NEI22330 | 33.80996 | -117.921 | WCO HOTELS INC | ANAHEIM, CA | TCA |  | 1.0 |  |  |  |  |
| NEI22332 | 33.85998 | -117.9011 | WEBER AIRCRAFT INC | FULLERTON, CA | TCA |  | 11147.2 |  |  |  |  |
| NEI22372 | 33.66382 | -116.2124 | ARMTEC DEFENSE PRODUCTS CO | COACHELLA, CA | MC | 1346.9 |  |  |  |  |  |
| NEI22375 | 33.86571 | -117.2582 | AURORA MODULAR INDUSTRIES INC | PERRIS, CA | TCA, PCE |  | 0.9 | 0.9 |  |  |  |
| NEI22379 | 34.0008 | -117.3376 | BOURNS INC | RIVERSIDE, CA | TCA |  | 3964.4 |  |  |  |  |
| NEI22429 | 33.87999 | -117.5309 | METRO LINE INDUSTRIES, INC, R. | CORONA, CA | TCA |  | 743.2 |  |  |  |  |
| NEI22430 | 33.84436 | -117.5115 | MINNESOTA MINING & MFG CO | CORONA, CA | TCA |  | 79.3 |  |  |  |  |
| NEI22450 | 33.88257 | -117.5967 | R SQUARED SCAN SYSTEMS, INC | CORONA, CA | TCA |  | 109.8 |  |  |  |  |
| NEI22458 | 33.9464 | -117.4612 | ROHR,INC | RIVERSIDE, CA | TCA |  | 10.5 |  |  |  |  |
| NEI22470 | 33.88168 | -117.5956 | TRANSCHEM, JETRONICS IND INC D | CORONA, CA | TCA |  | 2490.2 |  |  |  |  |
| NEI22474 | 33.89001 | -117.241 | US GOVT, AF DEPT, MARCH AFB (N | RIVERSIDE, CA | MC, TCA | 736.6 | 3166.1 |  |  |  |  |
| NEI22477 | 33.96998 | -117.361 | WESTERN POLYFORM CORP | RIVERSIDE, CA | TCA |  | 6486.0 |  |  |  |  |
| NEI22485 | 38.63185 | -121.2086 | AEROJET FINE CHEMICAL | RANCHO CORDOVA, CA | MC, PCE | 65.1 |  | 2.6 |  |  |  |
| NEI22495 | 38.52495 | -121.387 | APPARATUS UNLIMITED, INC. | SACRAMENTO, CA | TCA |  | 830.9 |  |  |  |  |
| NEI22652 | 38.59471 | -121.4911 | STATE OF CALIF PRINTING | SACRAMENTO, CA | TCA, PCE |  | 110.2 | 529.8 |  |  |  |
| NEI22679 | 38.49614 | -121.4553 | WORTHINGTON CHEV & MITSUBISHI | SACRAMENTO, CA | MC | 37.1 |  |  |  |  |  |
| NEI22709 | 33.99998 | -117.6711 | AMERICAN EAGLE WHEEL CORPORATI | CHINO, CA | TCA |  | 27151.1 |  |  |  |  |
| NEI22710 | 34.03765 | -117.5184 | AMERICAN SECURITY PRODUCTS CO | FONTANA, CA | TCA |  | 7303.7 |  |  |  |  |
| NEI22720 | 34.07998 | -117.541 | ARLON ELECTRONICS SUBSTRATES D | RANCHO CUCAMONGA, CA | TCA |  | 2520.8 |  |  |  |  |
| NEI22733 | 33.99999 | -117.701 | BRIGHT SHARK POWDER COATING | CHINO, CA | TCA |  | 3630.6 |  |  |  |  |
| NEI22744 | 34.07566 | -117.5012 | CALIFORNIA STEEL INDUSTRIES IN | FONTANA, CA | MC, TCA, PCE | 2077.9 | 0.1 | 0.5 |  |  |  |
| NEI22774 | 34.07995 | -117.2809 | FRANKLIN PRESS | SAN BERNARDINO, CA | TCA |  | 5.3 |  |  |  |  |
| NEI22776 | 34.05996 | -117.5409 | FRUIT GROWERS SUPPLY CO | ONTARIO, CA | TCA |  | 35.4 |  |  |  |  |
| NEI22787 | 34.08994 | -117.591 | GOODYEAR RUBBER CO,GOODYEAR RU | RANCHO CUCAMONGA, CA | TCA |  | 5887.6 |  |  |  |  |
| NEI22816 | 34.05 | -117.1909 | LA-Z-BOY WEST | REDLANDS, CA | TCA |  | 1044.6 |  |  |  |  |
| NEI22824 | 34.03996 | -117.631 | LOUD ENGINEERING & MFG INC | ONTARIO, CA | TCA |  | 3419.9 |  |  |  |  |
| NEI22848 | 35.6571 | -117.6621 | NAVAL AIR WEAPONS STATION | CHINA LAKE, CA, CA | MC, TCA, TCE, C Tetrachloride, Chloroform | 92.0 | 0.0 |  | 4.1 | 0.4 | 4.9 |
| NEI22866 | 34.06087 | -117.5262 | PRAXAIR INC | ONTARIO, CA | TCA |  | 544.3 |  |  |  |  |
| NEI22905 | 34.01992 | -117.561 | SPECTROL ELECTRONICS CORP | ONTARIO, CA | TCA |  | 355.6 |  |  |  |  |
| NEI22907 | 34.05796 | -117.6879 | SPRAYLINE ENTER. INC | ONTARIO, CA | MC, TCA | 44.9 | 3066.7 |  |  |  |  |
| NEI22925 | 34.00846 | -117.0648 | THE J. M. NEY CO | YUCAIPA, CA | TCA |  | 1039.6 |  |  |  |  |
| NEI22927 | 34.06091 | -117.5471 | THERMAL DYNAMICS CORP | ONTARIO, CA | TCA |  | 19776.6 |  |  |  |  |
| NEI22941 | 34.89492 | -116.8652 | USMC LOGISTICS BASE - YERMO | BARSTOW, CA | MC, TCA, PCE | 0.1 | 0.1 | 3.0 |  |  |  |
| NEI22952 | 34.09251 | -117.6361 | WESTERN MOULDINGS | UPLAND, CA | PCE |  |  | 38101.8 |  |  |  |
| NEI23077 | 32.68936 | -117.1344 | NATIONAL STEEL & SHIPBUILDING | SAN DIEGO, CA | PCE |  |  | 2.7 |  |  |  |
| NEI23188 | 33.24836 | -117.3993 | USMC BASE / CAMP PENDLETON | CAMP PENDLETON, CA | MC, TCA, PCE | 6.7 | 11.1 | 11.1 |  |  |  |
| NEI23392 | 37.77484 | -122.4117 | MONACO FILM LABS &VIDEO SERVIC | SAN FRANCISCO, CA | TCA |  | 7438.0 |  |  |  |  |
| NEI23404 | 37.74845 | -122.3968 | O'NEILL INC | SAN FRANCISCO, CA | TCA |  | 99.2 |  |  |  |  |
| NEI23510 | 37.75 | -122.435 | UNITED AIRLINES, MAINTENANCE O | SAN FRANCISCO, CA | PCE |  |  | 337.6 |  |  |  |
| NEI23615 | 37.85544 | -121.2642 | DEFENSE DISTRIB DEPOT SAN JOAQ | LATHROP, CA | TCA |  | 541.1 |  |  |  |  |
| NEI23692 | 37.71437 | -121.491 | OWENS-BROCKWAY GLASS CONTAINER | TRACY, CA | TCA |  | 12294.2 |  |  |  |  |
| NEI24080 | 37.56745 | -122.3119 | DURA FINISH OF SAN MATEO | SAN MATEO, CA | MC | 2423.1 |  |  |  |  |  |
| NEI24285 | 37.42085 | -122.2058 | STANFORD LINEAR ACCELERATOR | MENLO PARK, CA | TCA |  | 1756.1 |  |  |  |  |
| NEI24506 | 37.29918 | -121.8459 | APTEK INC | SAN JOSE, CA | TCA |  | 706.3 |  |  |  |  |
| NEI24755 | 37.36261 | -121.9502 | FMG ENTERPRISES INC | SANTA CLARA, CA | PCE |  |  | 339.1 |  |  |  |
| NEI24796 | 37.38322 | -121.9457 | HEDB CORPORATION | SANTA CLARA, CA | TCA |  | 158.0 |  |  |  |  |
| NEI24823 | 37.2022 | -121.8282 | IBM CORP, RESEARCH FACILITIES | SAN JOSE, CA | MC | 40.1 |  |  |  |  |  |
| NEI24980 | 37.38927 | -122.1005 | NASA-AMES RESEARCH CENTER | MOUNTAIN VIEW, CA | MC | 0.5 |  |  |  |  |  |
| NEI25016 | 37.27575 | -121.9434 | PACIFIC AEROSPACE SERVICES | CAMPBELL, CA | TCE |  |  |  | 1216.6 |  |  |
| NEI25038 | 37.41233 | -121.8871 | PECO CONTROLS CORP | MILPITAS, CA | TCA, TCE |  | 17.2 |  | 304.2 |  |  |
| NEI25148 | 37.40396 | -121.9094 | SENSYM | MILPITAS, CA | TCA |  | 0.0 |  |  |  |  |
| NEI25164 | 37.38192 | -121.962 | SILICONIX, INCORPORATED | SANTA CLARA, CA | TCA |  | 0.9 |  |  |  |  |
| NEI25212 | 37.38666 | -122.0321 | SUNPOWER CORPORATION | SUNNYVALE, CA | TCA |  | 9.1 |  |  |  |  |
| NEI25216 | 37.40512 | -122.023 | SUPERTEX, INC | SUNNYVALE, CA | TCA |  | 0.5 |  |  |  |  |
| NEI25245 | 37.37702 | -122.0284 | TOBAR INDUSTRIES | MOUNTAIN VIEW, CA | MC | 150.4 |  |  |  |  |  |
| NEI25264 | 37.23385 | -121.7415 | UNITED TECHNOLOGIES CORPORATIO | SAN JOSE, CA | MC, TCA | 25.2 | 644.1 |  |  |  |  |
| NEI25481 | 38.24466 | -122.0412 | OEA AREOSPACE INC | FAIRFIELD, CA | TCA |  | 152.3 |  |  |  |  |
| NEI25515 | 38.24686 | -121.9503 | TRAVIS AFB | TRAVIS AFB, CA | MC | 41.1 |  |  |  |  |  |
| NEI25756 | 38.43119 | -122.7147 | ZUMWALT MAGRINI CHRYSLER | SANTA ROSA, CA | MC | 55.3 |  |  |  |  |  |
| NEI25812 | 37.49707 | -120.853 | TRI VALLEY GROWERS CONTAINER D | MODESTO, CA | TCA |  | 96.4 |  |  |  |  |
| NEI25896 | 37.7327 | -120.9365 | SILGAN CONTAINERS MFR. CORP. | RIVERBANK, CA | MC, PCE | 64.0 |  | 256.3 |  |  |  |
| NEI25970 | 34.19186 | -118.9197 | AMGEN INC. | THOUSAND OAKS, CA | TCA, PCE |  | 161.4 | 49.0 |  |  |  |
| NEI25972 | 34.16334 | -119.2216 | ANACAPA MARINE SERVICE | OXNARD, CA | MC, TCA, PCE | 0.1 | 1.0 | 1.1 |  |  |  |
| NEI25980 | 34.2507 | -119.2271 | BELL POWDER COATING | VENTURA, CA | MC | 544.3 |  |  |  |  |  |
| NEI25984 | 34.14711 | -119.1713 | BMW - VEHICLE PREPARATION | OXNARD, CA | MC | 63.2 |  |  |  |  |  |
| NEI26000 | 34.20519 | -119.15 | ERG INTERNATIONAL | OXNARD, CA | TCA |  | 530.0 |  |  |  |  |
| NEI26004 | 34.22095 | -119.0722 | G & H TECHNOLOGY | CAMARILLO, CA | TCA |  | 150.4 |  |  |  |  |
| NEI26005 | 34.2498 | -119.2271 | GENERAL MAGNAPLATE CALIF. | VENTURA, CA | TCA |  | 2093.7 |  |  |  |  |
| NEI26006 | 34.28186 | -118.8738 | GENERAL OPTICS, INC. | MOORPARK, CA | TCA |  | 3120.4 |  |  |  |  |
| NEI26014 | 34.145 | -119.1886 | HUENEME BOAT WORKS | PORT HUENEME, CA | MC | 22.5 |  |  |  |  |  |
| NEI26022 | 34.28931 | -118.8577 | KAVLICO CORPORATION | MOORPARK, CA | MC, TCA | 1048.2 | 10287.4 |  |  |  |  |
| NEI26038 | 34.26987 | -118.7063 | NATEL ENGINEERING | SIMI VALLEY, CA | MC, TCA | 24.9 | 2582.8 |  |  |  |  |
| NEI26056 | 34.20701 | -119.1284 | PTI TECHNOLOGIES INC. | OXNARD, CA | MC, TCA | 40.2 | 464.2 |  |  |  |  |
| NEI26059 | 34.25851 | -119.2436 | ROBERT M. HADLEY CO. INC. | VENTURA, CA | TCA, PCE |  | 355.9 | 421.4 |  |  |  |
| NEI26060 | 34.24776 | -118.6754 | SANTA SUSANA FIELD LABORATORY | SIMI VALLEY, CA | TCA, TCE |  | 11485.7 |  | 3441.8 |  |  |
| NEI26084 | 34.21401 | -119.161 | ST. JOHN'S REGIONAL MEDICAL CT | OXNARD, CA | TCA |  | 37.4 |  |  |  |  |
| NEI26095 | 34.22134 | -119.1548 | TELAIR INTERNATIONAL | OXNARD, CA | TCA, PCE |  | 2060.0 | 3.5 |  |  |  |
| NEI26104 | 34.16156 | -119.2204 | PORT HUENEME SITE | PORT HUENEME, CA | TCA, PCE |  | 1.9 | 1.9 |  |  |  |
| NEI26183 | 39.10963 | -75.5553 | CAMDEL METALS CORPORATION | CAMDEN, DE | TCE |  |  |  | 5769.7 |  |  |
| NEI31242 | 41.08691 | -85.23862 | LINCOLN FOODSERVICE PRODUCTS, INC. | FORT WAYNE, IN | TCE |  |  |  | 70306.8 |  |  |
| NEI31360 | 39.03367 | -84.96786 | AURORA CASKET CO-VANGUARD PLT | AURORA, IN | TCE |  |  |  | 7194.0 |  |  |
| NEI31387 | 41.42172 | -84.86286 | THERMA-TRU CORPORATION | BUTLER, IN | MC | 6531.7 |  |  |  |  |  |
| NEI31662 | 39.6916 | -85.14228 | VISTEON SYSTEMS, LLC | CONNERSVILLE, IN | TCE |  |  |  | 874.1 |  |  |
| NEI31774 | 40.45714 | -86.10726 | DELPHI DELCO ELECTRONICS SYSTEMS | KOKOMO, IN | TCE |  |  |  | 4990.4 |  |  |
| NEI31789 | 40.86578 | -85.52287 | KEN-KOAT, INC. | HUNTINGTON, IN | TCE |  |  |  | 2488.9 |  |  |
| NEI32072 | 39.73353 | -86.21119 | ROLLS-ROYCE CORPORATION. PLANT 5 & 8 | INDIANAPOLIS, IN | PCE |  |  | 5619.8 |  |  |  |
| NEI32265 | 40.04 | -86.88 | RAYBESTOS | CRAWFORDSVILLE, IN | TCE |  |  |  | 12775.4 |  |  |
| NEI32399 | 41.465 | -86.49583 | AMERICAN ROLLER CO, LLC | WALKERTON, IN | MC | 2041.2 |  |  |  |  |  |
| NEI32428 | 41.65656 | -86.16654 | REMOTE CONTROLS, INC. | MISHAWAKA, IN | TCE |  |  |  | 1837.0 |  |  |
| NEI32786 | 39.02361 | -94.71445 | VITA CRAFT CORPORATION | SHAWNEE, KS | PCE |  |  | 15258.8 |  |  |  |
| NEI32801 | 38.3475 | -97.66917 | NATIONAL COOPERATIVE REFINERY ASSN | MC PHERSON, KS | TCA, PCE |  | 223.3 | 30.6 |  |  |  |
| NEI32829 | 37.66389 | -97.38389 | AIR CAPITOL PLATING, INC. | WICHITA, KS | TCE |  |  |  | 7194.0 |  |  |
| NEI32831 | 37.62417 | -97.28056 | BOEING COMMERCIAL AIRPLANE GROUP | WICHITA, KS | PCE, TCE |  |  | 18869.4 | 71214.0 |  |  |
| NEI32870 | 37.6811 | -85.91933 | AMBRAKE CORP | ELIZABETHTOWN, KY | TCE |  |  |  | 4798.9 |  |  |
| NEI33721 | 38.39566 | -75.59084 | PLYMOUTH TUBE COMPANY | SALISBURY, MD | TCE |  |  |  | 34701.6 |  |  |
| NEI34245 | 38.55189 | -91.00818 | SPORLAN VALVE COMPANY-PLANT #1 - EAST 7TH | WASHINGTON , MO | TCE |  |  |  | 3583.4 |  |  |
| NEI34246 | 38.56923 | -91.06091 | SPORLAN VALVE COMPANY-PLANT #3 - LANGE DRIVE | WASHINGTON , MO | TCE |  |  |  | 4088.7 |  |  |
| NEI34261 | 37.18927 | -93.32775 | CLARIANT LIFE SCIENCE MOLECULES-CLARIANT LIFE SCIE | SPRINGFIELD , MO | MC, Chloroform | 18.1 |  |  |  |  | 3.6 |
| NEI34377 | 38.95902 | -94.57657 | U. S. DEPT OF ENERGY-KANSAS CITY PLANT (ALLIEDSIGN | KANSAS CITY , MO | PCE |  |  | 21.9 |  |  |  |
| NEI34386 | 37.09454 | -94.52769 | EAGLE-PICHER TECHNOLOGIES LLC-FEDERAL SYSTEMS | JOPLIN , MO | TCE |  |  |  | 914.0 |  |  |
| NEI34395 | 37.06268 | -94.46952 | MIDCON CABLES COMPANY-MIDCON CABLES COMPANY | JOPLIN , MO | MC | 392.7 |  |  |  |  |  |
| NEI34460 | 38.97669 | -91.50786 | UNIQUE AUTOMOTIVE REBUILDERS INC-JONESBURG | JONESBURG , MO | TCE |  |  |  | 4445.2 |  |  |
| NEI34485 | 37.74723 | -89.86833 | SABRELINER CORPORATION-PERRYVILLE PLANT | PERRYVILLE , MO | TCA |  | 0.8 |  |  |  |  |
| NEI34493 | 38.71115 | -93.19415 | MISSOURI PRESSED METALS INC-SEDALIA | SEDALIA , MO | TCE |  |  |  | 37848.2 |  |  |
| NEI34514 | 39.29744 | -94.69372 | AMERICAN AIRLINES-MCI MAINTENANCE AND ENGINEERING | KANSAS CITY , MO | PCE |  |  | 2103.3 |  |  |  |
| NEI34540 | 38.81151 | -90.47327 | MCDONNELL DOUGLAS CORP-BOEING COMPANY | ST. CHARLES , MO | TCE |  |  |  | 2162.5 |  |  |
| NEI34632 | 38.75964 | -90.36317 | MCDONNELL DOUGLAS CORP./BOEING COMPANY-LINDBERGH P | ST. LOUIS , MO | TCA, TCE |  | 207.9 |  | 5510.4 |  |  |
| NEI34658 | 38.59393 | -90.49836 | DANA CORPORATION-PERFECT CIRCLE DIVISION | MANCHESTER , MO | TCE |  |  |  | 72889.1 |  |  |
| NEI34673 | 38.61293 | -90.33203 | SUNNEN PRODUCTS COMPANY-MAPLEWOOD | MAPLEWOOD , MO | PCE |  |  | 4164.0 |  |  |  |
| NEI34682 | 38.73506 | -90.35028 | AMERICAN AIRLINES INC-OLD NATURAL BRIDGE RD | ST. LOUIS , MO | MC, PCE | 1.2 |  | 20.0 |  |  |  |
| NEI34730 | 38.62001 | -90.28055 | ALLIED HEALTH CARE PRODUCTS-ALLIED HEALTH CARE PRO | ST. LOUIS , MO | TCE |  |  |  | 3810.2 |  |  |
| NEI34784 | 38.57306 | -90.23387 | OTTEN SCREW PRODUCTS CO-OTTEN SCREW PRODUCTS CO | ST. LOUIS , MO | PCE |  |  | 98.9 |  |  |  |
| NEI35612 | 42.3 | -75.39 | AMPHENOL CORP - BENDIX CONNECTOR OPERS | SIDNEY, NY | TCE |  |  |  | 28294.6 |  |  |
| NEI36095 | 40.66 | -73.9 | ARROW LOCK MANUFACTURING CO | BROOKLYN, NY | TCE |  |  |  | 7021.6 |  |  |
| NEI36181 | 40.725 | -74 | CARTER SPRAY FINISHING CORP. | BROOKLYN, NY | TCE |  |  |  | 3904.1 |  |  |
| NEI37022 | 43.2 | -77.64 | KODAK PARK DIVISION | ROCHESTER, NY | MC | 92.1 |  |  |  |  |  |
| NEI38155 | 43.08472 | -75.25417 | INDIUM CORP. OF AMERICA | UTICA, NY | TCE |  |  |  | 2098.8 |  |  |
| NEI39761 | 40.7 | -73.37 | LAWRENCE RIPAK FACILITY | BABYLON, NY | PCE |  |  | 6156.6 |  |  |  |
| NEI40416 | 41.41035 | -81.78436 | WELLMAN FRICTION PRODUCTS BROOK PARK | BROOK PARK, OH | PCE |  |  | 443.0 |  |  |  |
| NEI40611 | 44.65468 | -123.0632 | WAH CHANG | ALBANY, OR | TCA |  | 1560.2 |  |  |  |  |
| NEI41241 | 32.84656 | -80.0055 | INDUSTRIAL CONTAINER SERVICES | CHARLESTON, SC | MC | 1850.7 |  |  |  |  |  |
| NEI41252 | 32.89 | -79.97 | MEADWESTVACO CORPORATION INC | NORTH CHARLESTON, SC | PCE |  |  | 0.4 |  |  |  |
| NEI41338 | 34.68729 | -82.23283 | KEMET:FOUNTAIN INN | FOUNTAIN INN, SC | MC | 1451.5 |  |  |  |  |  |
| NEI42005 | 41.66667 | -112.4333 | PROMONTORY PLANT | PROMONTORY, UT | MC, TCA, TCE, Chloroform | 2410.8 | 16954.4 |  | 571.1 |  | 1682.9 |
| NEI42018 | 41.11694 | -111.9769 | MAIN BASE | HILL AIR FORCE BASE, UT | MC, TCA, PCE, TCE, Chloroform | 99.5 | 3.1 | 202.4 | 7.2 |  | 22.5 |
| NEI42400 | 47.75566 | -117.3869 | TRAVIS PATTERN | SPOKANE, WA | TCE |  |  |  | 1505.5 |  |  |
| NEI42671 | 44.08027 | -87.70291 | FOSTER NEEDLE CO., INC. | MANITOWOC, WI | TCE |  |  |  | 13257.6 |  |  |
| NEI42701 | 44.8938 | -87.89551 | CERA-MITE CORPORATION | OCONTO, WI | TCE |  |  |  | 2799.1 |  |  |
| NEI42711 | 43.31797 | -87.95909 | VISHAY CERA-MITE CORPORATION | GRAFTON, WI | TCE |  |  |  | 2137.3 |  |  |
| NEI42750 | 42.72706 | -87.79069 | RACINE PLATING CO. | RACINE, WI | TCE |  |  |  | 1411.8 |  |  |
| NEI43004 | 43.63196 | -88.73459 | NATIONAL RIVET & MANUFACTURING COMPANY | WAUPUN, WI | TCE |  |  |  | 3352.0 |  |  |
| NEI43378 | 36.1204 | -86.69345 | VOUGHT AIRCRAFT INDUSTRIES, INC | NASHVILLE, TN | MC, TCE | 32.7 |  |  | 6509.0 |  |  |
| NEI43707 | 35.51483 | -78.30653 | ANDREW CORPORATION NORTH CAROLINA | SMITHFIELD, NC | TCA |  | 2.0 |  |  |  |  |
| NEI44511 | 45.2135 | -93.4113 | IMI CORNELIUS INC | ANOKA, MN | TCE |  |  |  | 1186.1 |  |  |
| NEI44674 | 36.08058 | -79.24723 | AKG OF AMERICA INC | MEBANE, NC | PCE |  |  | 11905.9 |  |  |  |
| NEI44730 | 44.915 | -93.4156 | KANGAS ENAMELING INC | HOPKINS, MN | TCE |  |  |  | 898.1 |  |  |
| NEI45064 | 35.1599 | -79.0046 | HQ XVIII ABN CORPS & FORT BRAGG | FORT BRAGG, NC | MC | 6.4 |  |  |  |  |  |
| NEI45127 | 41.78334 | -71.51759 | MEARTHANE PRODUCTS CORPORATION | CRANSTON, RI | MC | 4354.5 |  |  |  |  |  |
| NEI45203 | 34.92278 | -76.88944 | MARINE CORPS AIR STATION | CHERRY POINT, NC | MC, TCA, PCE | 83.6 | 2.2 | 6.0 |  |  |  |
| NEI45208 | 34.8936 | -76.8967 | NAVAL AIR DEPOT | CHERRY POINT, NC | MC | 8935.8 |  |  |  |  |  |
| NEI45456 | 44.9892 | -93.257 | SUPERIOR PLATING INC | MINNEAPOLIS, MN | TCE |  |  |  | 900.4 |  |  |
| NEI45529 | 41.81747 | -71.44441 | CATHEDRAL ART METAL CO., INC. | PROVIDENCE, RI | MC | 165.1 |  |  |  |  |  |
| NEI45542 | 41.79122 | -71.40076 | RIBCO MFG. INC. (PROVIDENCE) | PROVIDENCE, RI | TCE |  |  |  | 694.0 |  |  |
| NEI46603 | 47.55361 | -122.3297 | ART BRASS PLATING INC. | SEATTLE, WA | TCE |  |  |  | 7105.5 |  |  |
| NEI47624 | 41.7639 | -87.7483 | KASTALON INC | ALSIP, IL | TCE |  |  |  | 7184.9 |  |  |
| NEI48022 | 41.94 | -87.8769 | GRAPH-ON INC | FRANKLIN PARK, IL | TCE |  |  |  | 3628.7 |  |  |
| NEI48035 | 41.938 | -87.884 | AMERICAN RIVET CO | FRANKLIN PARK, IL | TCE |  |  |  | 7030.7 |  |  |
| NEI48062 | 41.95207 | -87.88914 | SLOAN VALVE CO | FRANKLIN PARK, IL | TCE |  |  |  | 4189.0 |  |  |
| NEI48274 | 42.01843 | -87.7885 | STIMSONITE CORP | NILES, IL | TCE |  |  |  | 1796.2 |  |  |
| NEI48296 | 42.0344 | -87.8961 | ADAMS ELEVATOR EQUIPMENT CO | NILES, IL | TCE |  |  |  | 2698.3 |  |  |
| NEI48353 | 42.099 | -88.0381 | ARLINGTON PLATING CO | PALATINE, IL | TCE |  |  |  | 22162.2 |  |  |
| NEI48419 | 42.022 | -87.964 | METAL IMPACT CORP | ELK GROVE VILLAGE, IL | PCE |  |  | 4717.4 |  |  |  |
| NEI48445 | 41.9658 | -87.8728 | CASTLE METAL FINISHING CORP | SCHILLER PARK, IL | TCE |  |  |  | 8519.6 |  |  |
| NEI48447 | 41.9673 | -87.866 | WISCONSIN TOOL & STAMPING CO | SCHILLER PARK, IL | TCE |  |  |  | 7224.5 |  |  |
| NEI48568 | 42.12964 | -87.923 | SUNNYSIDE CORP | WHEELING, IL | MC | 7889.5 |  |  |  |  |  |
| NEI48613 | 41.9895 | -88.1783 | SENIOR FLEXONICS INC | BARTLETT, IL | TCE |  |  |  | 60290.5 |  |  |
| NEI48676 | 42.004 | -87.9645 | MAGNETIC INSPECTION LABORATORIES INC | ELK GROVE VILLAGE, IL | TCE |  |  |  | 6214.2 |  |  |
| NEI48889 | 41.9406 | -87.6931 | HU-FRIEDY MANUFACTURING CO | CHICAGO, IL | TCE |  |  |  | 1278.7 |  |  |
| NEI48914 | 41.9158 | -87.7475 | PARKVIEW METAL PRODUCTS | CHICAGO, IL | TCE |  |  |  | 1981.3 |  |  |
| NEI49391 | 41.95 | -87.6628 | CRAFTSMAN PLATING & TINNING CORP | CHICAGO, IL | TCE |  |  |  | 3396.5 |  |  |
| NEI49427 | 41.8853 | -87.6575 | AMERICAN NICKEL WORKS | CHICAGO, IL | TCE |  |  |  | 12389.9 |  |  |
| NEI49525 | 41.9288 | -87.7316 | GENERAL MACHINERY & MANUFACTURING CO | CHICAGO, IL | TCE |  |  |  | 4017.5 |  |  |
| NEI49526 | 41.8056 | -87.7089 | L & M CAST STONE INC | CHICAGO, IL | TCE |  |  |  | 4123.0 |  |  |
| NEI49625 | 41.8539 | -87.73637 | ABLE ELECTROPOLISHING CO | CHICAGO, IL | TCE |  |  |  | 20894.2 |  |  |
| NEI50167 | 41.7389 | -87.9375 | MEADEN SCREW PRODUCTS CO | BURR RIDGE, IL | TCE |  |  |  | 4039.1 |  |  |
| NEI51064 | 41.6716 | -88.5376 | PLANO METAL SPECIALTIES INC | PLANO, IL | TCE |  |  |  | 1132.2 |  |  |
| NEI51726 | 42.2447 | -88.32 | JOHN CRANE INC | CRYSTAL LAKE, IL | TCE |  |  |  | 2434.9 |  |  |
| NEI51753 | 42.175 | -88.4286 | UNION SPECIAL CORP | HUNTLEY, IL | TCE |  |  |  | 296.6 |  |  |
| NEI52191 | 38.68577 | -90.1665 | SPECTRULITE CONSORTIUM INC | MADISON, IL | TCE |  |  |  | 512.6 |  |  |
| NEI52497 | 42.1294 | -89.257 | QUALITY METAL FINISHING CO | BYRON, IL | TCE |  |  |  | 71985.6 |  |  |
| NEI53014 | 38.59196 | -90.1724 | CERRO COPPER PRODUCTS CO | SAUGET, IL | TCE |  |  |  | 41639.1 |  |  |
| NEI53153 | 39.85 | -89.2786 | FORMOSA PLASTICS CORPORATION | ILLIOPOLIS, IL | TCE |  |  |  | 4.0 |  |  |
| NEI53352 | 40.14204 | -87.6137 | DANVILLE METAL STAMPING CO | DANVILLE, IL | PCE |  |  | 79.5 |  |  |  |
| NEI53562 | 41.6274 | -89.9538 | STERLING MULTI PRODUCTS | PROPHETSTOWN, IL | TCE |  |  |  | 3078.1 |  |  |
| NEI53688 | 41.4483 | -87.751 | FEDERAL SIGNAL CORP SIGNAL DIVISION | UNIVERSITY PARK, IL | TCE |  |  |  | 7885.7 |  |  |
| NEI53702 | 41.64441 | -88.0558 | CITGO PETROLEUM CORP | LEMONT, IL | TCA |  | 1481.3 |  |  |  |  |
| NEI54141 | 36.11628 | -86.74124 | SAFETY KLEEN | NASHVILLE, TN | PCE |  |  | 0.4 |  |  |  |
| NEI54795 | 41.9492 | -87.8686 | ACRA ELECTRIC CORP | SCHILLER PARK, IL | MC, TCE | 5183.7 |  |  | 1358.2 |  |  |
| NEI54855 | 42.0211 | -87.9621 | ACME FINISHING CO | ELK GROVE VILLAGE, IL | TCE |  |  |  | 3592.5 |  |  |
| NEI54885 | 41.9806 | -87.7628 | SWITCHCRAFT INC | CHICAGO, IL | TCE |  |  |  | 3311.2 |  |  |
| NEI54963 | 41.9189 | -87.6631 | CLYBOURN METAL FINISHING CO | CHICAGO, IL | TCE |  |  |  | 4626.2 |  |  |
| NEI55239 | 41.80156 | -88.0626 | LOCKFORMER CO | LISLE, IL | TCE |  |  |  | 16963.6 |  |  |
| NEI55719 | 42.4383 | -88.2497 | INTERMATIC INC | SPRING GROVE, IL | TCE |  |  |  | 8491.8 |  |  |
| NEI55774 | 39.8206 | -88.9653 | ZEXEL VALEO COMPRESSOR USA | DECATUR, IL | TCE |  |  |  | 1864.3 |  |  |
| NEI56886 | 43.18659 | -85.23751 | NORTHLAND CORP | GREENVILLE, MI | MC | 552.8 |  |  |  |  |  |
| NEI2CA033118 | 37.37386 | -122.0002 | HEWLETT-PACKARD | SUNNYVALE, CA | TCA |  | 0.5 |  |  |  |  |
| NEI2CA124904 | 34.02788 | -118.2365 | LOS ANGELES TIMES | LOS ANGELES, CA | TCA, PCE |  | 25.1 | 25.1 |  |  |  |
| NEI2CA130344 | 33.90549 | -118.2741 | CONFLUENCE FMC, INC- HARDEN INDUSTRIES | LOS ANGELES, CA | MC, PCE | 1653.3 |  | 4305.5 |  |  |  |
| NEI2CA133660 | 33.87997 | -117.5901 | HAYDEN INDUSTRIAL PRODUCTS | CORONA, CA | MC, TCA, PCE, TCE | 0.7 | 6383.6 | 0.4 | 0.7 |  |  |
| NEI2CA251063 | 34.4317 | -119.9075 | VENOCO - ELLWOOD | GOLETA, CA | PCE |  |  | 5.4 |  |  |  |
| NEI2CA271567 | 33.07683 | -116.6 | NORMS SERVICE | JULIAN, CA | MC, TCA, PCE | 0.0 | 0.0 | 0.0 |  |  |  |
| NEI2CA272317 | 32.7872 | -116.9774 | SPECIALIZED PROCESSING CO., IN | EL CAJON, CA | PCE |  |  | 1347.2 |  |  |  |
| NEI2CA274026 | 32.71934 | -117.225 | DRISSCOLL BOAT WORKS | SAN DIEGO, CA | MC | 66.9 |  |  |  |  |  |
| NEI2CA275448 | 32.71032 | -117.2249 | DRISCOLL CUSTOM BOATS | SAN DIEGO, CA | MC | 124.6 |  |  |  |  |  |
| NEI2CA512150 | 34.94853 | -117.888 | NASA DRYDEN FLIGHT RESEARCH CR | EDWARDS AFB, CA | TCA, PCE |  | 24.5 | 1.3 |  |  |  |
| NEI2CA789244 | 32.75657 | -117.2199 | STRIP SHOP THE | SAN DIEGO , CA | MC | 2097.4 |  |  |  |  |  |
| NEI2CA791411 | 33.13667 | -117.2217 | PENNYSAVER SOUTHERN COMPRINT C | VISTA, CA | MC, TCA, PCE | 0.3 | 0.5 | 0.5 |  |  |  |
| NEI2CA798094 | 32.81765 | -116.9623 | DAVES CUSTOM BOATS | EL CAJON, CA | MC, TCA, PCE | 0.0 | 0.0 | 0.0 |  |  |  |
| NEI2CA798332 | 33.14789 | -117.233 | DIMENSION ONE SPAS | VISTA, CA | MC | 34.0 |  |  |  |  |  |
| NEI2CO123356 | 40.08268 | -104.9845 | PCC COMPOSITES | FREDERICK, CO | TCE |  |  |  | 2086.5 |  |  |
| NEI2CO1235 | 39.98406 | -105.0901 | ROCKY MOUNTAIN INSTRUMENT | LAFAYETTE, CO | MC | 563.8 |  |  |  |  |  |
| NEI2CO1238 | 40.03458 | -105.2333 | VECTOR CORPORATION | BOULDER, CO | TCE |  |  |  | 669.5 |  |  |
| NEI2IL005AMV | 41.933 | -88.042 | ADVANCE WIRE PRODUCTS/JASON COMPONENTS GROUP | ADDISON, IL | TCE |  |  |  | 5143.7 |  |  |
| NEI2IL015APF | 39.8489 | -88.9866 | FAIRLAWN CEMETERY | DECATUR, IL | TCE |  |  |  | 4853.4 |  |  |
| NEI2IL045AAP | 42.071 | -88.498 | ELECTRO-MAX INC | HAMPSHIRE, IL | TCE |  |  |  | 907.1 |  |  |
| NEI2IL060AAX | 41.796 | -88.34 | HASSE & WREDE NORTH AMERICA | NORTH AURORA, IL | TCE |  |  |  | 3719.8 |  |  |
| NEI2IL096ANM | 41.942 | -87.903 | CASTING IMPREGNATORS INC | FRANKLIN PARK, IL | TCE |  |  |  | 3113.5 |  |  |
| NEI2IL153ACB | 41.8195 | -87.863 | BILLET SPECIALTIES INC | LAGRANGE, IL | TCE |  |  |  | 1161.2 |  |  |
| NEI2IL186AHK | 41.8958 | -87.8667 | MILLENNIUM POLISHERS INC | MELROSE PARK, IL | TCE |  |  |  | 979.8 |  |  |
| NEI2IL186AHR | 41.9006 | -87.8639 | JAY-TEE SCREW MACHINE PRODUCTS CO | MELROSE PARK, IL | TCE |  |  |  | 2264.3 |  |  |
| NEI2IL195AAA | 41.7712 | -89.7293 | ARRIS INTERNATIONAL INC | ROCK FALLS, IL | PCE |  |  | 67086.3 |  |  |  |
| NEI2IL306AAP | 42.018 | -88.147 | STREAMWOOD PLATING CO | STREAMWOOD, IL | TCE |  |  |  | 2245.5 |  |  |
| NEI2IL440AMC | 41.9954 | -87.9637 | PMB HYDRA-SCREW | ELK GROVE VILLAGE, IL | MC | 2238.9 |  |  |  |  |  |
| NEI2IL489AAP | 42.001 | -88.103 | TWR SERVICE CORP | SCHAUMBURG, IL | TCE |  |  |  | 1193.5 |  |  |
| NEI2IN097373 | 39.74834 | -86.25833 | PARTS CLEANING TECHNOLOGIES, LLC | INDIANAPOLIS, IN | TCE |  |  |  | 2510.8 |  |  |
| NEI2KY300045 | 36.7075 | -86.56944 | PETROFERM INCORPORATED | FRANKLIN, KY | TCE |  |  |  | 5089.3 |  |  |
| NEI2MIM4579 | 42.19792 | -83.24402 | AIR TAYLOR MACHINES | TAYLOR, MI | TCA |  | 177.6 |  |  |  |  |
| NEI2MIN0081 | 42.47786 | -83.08003 | PAINT WORK INC | WARREN, MI | TCE |  |  |  | 2719.0 |  |  |
| NEI2MIN3023 | 42.47653 | -83.09569 | ELECTRO PLATING SERVICES INC | MADISON HTS, MI | TCE |  |  |  | 7304.7 |  |  |
| NEI2MIN5810 | 42.27977 | -83.81072 | KAISER OPTICAL SYSTEMS INC | ANN ARBOR, MI | MC, TCE | 21.1 |  |  | 3.0 |  |  |
| NEI2MIN6857 | 42.46835 | -82.9869 | PPI AEROSPACE ACQUISITION, LLC | WARREN, MI | TCE |  |  |  | 4504.3 |  |  |
| NEI2MIN6858 | 42.46473 | -82.99677 | PPI AEROSPACE ACQUISITION, LLC | WARREN, MI | TCE |  |  |  | 1071.1 |  |  |
| NEI2MIN6937 | 42.23297 | -83.73576 | TECUMSEH PRODUCTS CO | ANN ARBOR, MI | TCE |  |  |  | 76.9 |  |  |
| NEI2MIN7048 | 42.81579 | -82.97885 | 20TH CENTURY MACHINE COMPANY INC | ARMADA, MI | TCE |  |  |  | 1563.8 |  |  |
| NEI2MN109084 | 44.0461 | -92.5128 | MAYO MEDICAL CENTER - ROCHESTER | ROCHESTER, MN | TCA |  | 96.2 |  |  |  |  |
| NEI2MN700294 | 44.868 | -93.1722 | LCS CO | ST. PAUL, MN | TCE |  |  |  | 1503.3 |  |  |
| NEI2MO071019 | 38.48931 | -90.76166 | CDEX INC-CDEX INC | PACIFIC , MO | TCE |  |  |  | 2024.8 |  |  |
| NEI2MO071132 | 38.5715 | -91.03654 | SPORLAN VALVE COMPANY-PLANT #2 - WEST MAIN | WASHINGTON , MO | TCE |  |  |  | 4217.0 |  |  |
| NEI2MO077236 | 37.21788 | -93.29386 | POSITRONIC INDUSTRIES INC-SPRINGFIELD | SPRINGFIELD , MO | TCE |  |  |  | 601.7 |  |  |
| NEI2MO115005 | 39.70562 | -92.95192 | MOORE COMPANY-MOORE COMPANY | MARCELINE , MO | TCE |  |  |  | 181.9 |  |  |
| NEI2MO1489 | 38.77651 | -90.36434 | GKN AEROSPACE SERVICES INC-BERKELEY | HAZELWOOD , MO | TCE |  |  |  | 4682.9 |  |  |
| NEI2MO183018 | 38.72368 | -90.7148 | COMPONENT BAR PRODUCTS INC-ST. CHARLES | ST. CHARLES , MO | TCE |  |  |  | 16260.8 |  |  |
| NEI2MO189278 | 38.53421 | -90.44338 | MAGNETIC POWER SYSTEMS INC-MANUFACTURERS DRIVE | FENTON , MO | TCE |  |  |  | 604.2 |  |  |
| NEI2MO510094 | 38.5514 | -90.26304 | LOOSE LEAF HARDWARE MFG CO-QUICK ACTION DIV | ST. LOUIS , MO | TCE |  |  |  | 603.7 |  |  |
| NEI2NC00071 | 36.0649 | -80.2273 | CORRFLEX DISPLAY AMD PACKAGING | WINSTON-SALEM, NC | TCA, PCE |  | 1.8 | 1.8 |  |  |  |
| NEI2OK5092 | 34.7874 | -96.67337 | APEX COMPOSITES INC | ADA, OK | TCE |  |  |  | 907.2 |  |  |
| NEI2RIAIR13 | 41.94864 | -71.46571 | A.T. CROSS COMPANY | LINCOLN, RI | MC, TCE | 1745.0 |  |  | 206.4 |  |  |
| NEI2RIAIR152 | 41.79131 | -71.40148 | BEAUCRAFT, INC. | PROVIDENCE, RI | TCE |  |  |  | 684.0 |  |  |
| NEI2RIAIR19 | 41.73714 | -71.44631 | A.T. WALL CO. | WARWICK, RI | PCE, TCE |  |  | 476.7 | 206.8 |  |  |
| NEI2RIAIR224 | 42.00914 | -71.5307 | EASTERN RESINS CORP. | WOONSOCKET, RI | MC | 140.6 |  |  |  |  |  |
| NEI2RIAIR245 | 41.77709 | -71.42601 | CENTRAL TOOLS, INC. | CRANSTON, RI | TCE |  |  |  | 571.5 |  |  |
| NEI2RIAIR325 | 41.93474 | -71.44917 | CREST MANUFACTURING CO. | LINCOLN, RI | PCE |  |  | 99.8 |  |  |  |
| NEI2RIAIR354 | 41.79506 | -71.4866 | DANECRAFT, INC. | PROVIDENCE, RI | MC | 15.0 |  |  |  |  |  |
| NEI2RIAIR355 | 41.8756 | -71.38799 | DARLENE JEWELRY MFG. | PAWTUCKET, RI | TCE |  |  |  | 818.7 |  |  |
| NEI2RIAIR409 | 41.73169 | -71.44588 | DROITCOUR CO. | WARWICK, RI | TCE |  |  |  | 363.8 |  |  |
| NEI2RIAIR475 | 41.8169 | -71.44662 | ELI METAL PRODUCTS | PROVIDENCE, RI | TCE |  |  |  | 909.9 |  |  |
| NEI2RIAIR570 | 41.85156 | -71.48582 | G. TANURY PLATING COMPANY | JOHNSTON, RI | TCA |  | 5.4 |  |  |  |  |
| NEI2RIAIR673 | 41.80686 | -71.40847 | HERFF JONES INC. | PROVIDENCE, RI | MC, TCE | 92.1 |  |  | 346.5 |  |  |
| NEI2RIAIR717 | 41.82946 | -71.37051 | IMPCO, INC. | EAST PROVIDENCE, RI | TCE |  |  |  | 245.4 |  |  |
| NEI2RIAIR74 | 41.81904 | -71.3746 | AMERICAN RING CO. | EAST PROVIDENCE, RI | MC | 48.5 |  |  |  |  |  |
| NEI2RIAIR740 | 41.79017 | -71.40347 | INTERNATIONAL INSIGNIA CORP. | PROVIDENCE, RI | TCE |  |  |  | 11.3 |  |  |
| NEI2RIAIR748 | 41.74704 | -71.44849 | ISELANN-MOSS IND., INC. | CRANSTON, RI | MC | 272.2 |  |  |  |  |  |
| NEI2RIAIR811 | 41.81462 | -71.44171 | KAROWAY POLISHING, INC. | PROVIDENCE, RI | TCE |  |  |  | 435.4 |  |  |
| NEI2RIAIR874 | 41.87238 | -71.40881 | LEVIN PLATING CO. | PAWTUCKET, RI | TCE |  |  |  | 1516.8 |  |  |
| NEI2RIAIR987 | 41.83032 | -71.43074 | MICROFIN CORP. | PROVIDENCE, RI | TCE |  |  |  | 1333.1 |  |  |
| NEI2RIIR1109 | 41.87888 | -71.3984 | NULCO MFG. CO. | PAWTUCKET, RI | TCE |  |  |  | 1306.3 |  |  |
| NEI2RIIR1110 | 41.81412 | -71.44159 | NU-LUSTRE CORPORATION | PROVIDENCE, RI | TCE |  |  |  | 151.5 |  |  |
| NEI2RIIR1230 | 41.8717 | -71.41236 | PROVIDENCE METALLIZING CO., INC. | PAWTUCKET, RI | TCE |  |  |  | 5656.7 |  |  |
| NEI2RIIR1266 | 41.79584 | -71.479 | R & R POLISHING CO. INC. | CRANSTON, RI | TCE |  |  |  | 827.4 |  |  |
| NEI2RIIR1483 | 41.85713 | -71.34505 | TANYA CREATIONS, INC. | EAST PROVIDENCE, RI | MC | 125.2 |  |  |  |  |  |
| NEI2RIIR1660 | 41.88656 | -71.40331 | WHITTET-HIGGINS CO. | CENTRAL FALLS, RI | TCE |  |  |  | 1983.6 |  |  |
| NEI2RIIR1831 | 41.86448 | -71.40153 | MASBRO POLISHING COMPANY | PAWTUCKET, RI | TCE |  |  |  | 1236.5 |  |  |
| NEI2RIIR1838 | 41.88346 | -71.38269 | MEL-CO-ED INC. | PAWTUCKET, RI | TCE |  |  |  | 1496.9 |  |  |
| NEI2RIIR2579 | 41.75077 | -71.43787 | KEARFLEX ENGINEERING | WARWICK, RI | TCE |  |  |  | 1152.1 |  |  |
| NEI2RIIR2703 | 41.80079 | -71.4382 | COTO CORPORATION | PROVIDENCE, RI | TCE |  |  |  | 1213.4 |  |  |
| NEI2RIIR2874 | 41.82513 | -71.47113 | E & M ENTERPRISES LTD | JOHNSTON, RI | TCE |  |  |  | 1197.5 |  |  |
| NEI2RIIR2881 | 41.79673 | -71.48087 | TIME POLISHING | JOHNSTON, RI | TCA |  | 5.1 |  |  |  |  |
| NEI2RIIR3014 | 41.90099 | -71.39464 | TEKNICOTE, INC. (CUMBERLAND) | CUMBERLAND, RI | TCE |  |  |  | 2767.7 |  |  |
| NEI2RIIR3168 | 41.80622 | -71.43062 | SALVADORE TOOL & FINDINGS INC. | PROVIDENCE, RI | TCE |  |  |  | 235.9 |  |  |
| NEI2RIIR3264 | 41.88663 | -71.38283 | SANFORD WHITE CO., INC. | CENTRAL FALLS, RI | TCE |  |  |  | 220.4 |  |  |
| NEI2RIIR3506 | 41.7947 | -71.40729 | R I HEAT TREATING COMPANY | PROVIDENCE, RI | TCE |  |  |  | 299.4 |  |  |
| NEI2RIIR3542 | 41.79152 | -71.40035 | IRA GREEN | PROVIDENCE, RI | TCE |  |  |  | 3829.2 |  |  |
| NEI2RIIR3572 | 41.83924 | -71.42012 | DREW EASTON CO., INC. | PROVIDENCE, RI | MC | 28.2 |  |  |  |  |  |
| NEI2RIIR3616 | 41.66795 | -71.27788 | RUSS-RUSS REALTY/ROBIN ROY | BRISTOL, RI | TCE |  |  |  | 358.3 |  |  |
| NEI2SC0-0175 | 34.97169 | -81.99141 | HOKE INC | SPARTANBURG, SC | MC | 2103.8 |  |  |  |  |  |
| NEI2SC0-0266 | 34.94708 | -81.98814 | ENGELHARD:DUNCAN | DUNCAN, SC | PCE |  |  | 478.5 |  |  |  |
| NEI2TX11369 | 32.82056 | -96.84306 | FOREST PARK FACILITY | DALLAS, TX | TCE |  |  |  | 2948.3 |  |  |
| NEI2UT11674 | 40.77917 | -111.9597 | SKYWEST AIRLINES AT SLC INT'L AIRPORT | SALT LAKE CITY, UT | TCA |  | 15.0 |  |  |  |  |
| NEI2WI243310 | 42.9855 | -87.91421 | ELITE FINISHING, LLC | MILWAUKEE, WI | TCE |  |  |  | 2812.3 |  |  |
| NEIART$10939 | 36.18904 | -94.10984 | AMERICAN TUBING,INCORPORATED | SPRINGDALE, AR | TCE |  |  |  | 12791.3 |  |  |
| NEICA001271 | 37.50939 | -121.9486 | MENLO INDUSTRIES, INC | FREMONT, CA | TCA |  | 6.1 |  |  |  |  |
| NEICA00160 | 37.74224 | -122.2148 | ROLLS-ROYCE ENGINE SERVICES - | OAKLAND, CA | TCE |  |  |  | 1058.5 |  |  |
| NEICA013629 | 37.92973 | -122.0259 | VARIAN CHROMATOGRAPHY SYSTEMS | WALNUT CREEK, CA | PCE |  |  | 126.4 |  |  |  |
| NEICA0263624 | 34.12999 | -118.261 | RALPHS GROCERY CO | LOS ANGELES, CA | TCA |  | 1.3 |  |  |  |  |
| NEICA029988 | 35.42009 | -119.064 | PACTIV CORPORATION | BAKERSFIELD, CA | TCA |  | 7208.0 |  |  |  |  |
| NEICA0333180 | 38.92595 | -122.6149 | LAKE COUNTY CLEANERS/LOWER LAK | LOWER LAKE, CA | PCE |  |  | 137.9 |  |  |  |
| NEICA0333190 | 39.04599 | -122.9151 | LAKE COUNTY CLEANERS/LAKEPORT | LAKEPORT, CA | PCE |  |  | 252.7 |  |  |  |
| NEICA0371139 | 34.24996 | -118.3911 | LA CO., METROPOLITAN TRANS AUT | SUN VALLEY, CA | TCA |  | 441.2 |  |  |  |  |
| NEICA0371143 | 34.2368 | -118.5961 | SCHAEFFER MAGNETICS INC | CHATSWORTH, CA | TCA |  | 182.2 |  |  |  |  |
| NEICA0371152 | 34.09554 | -117.7402 | LOCKHEED MARTIN ELECTRO-OPTICA | POMONA, CA | TCA |  | 7194.4 |  |  |  |  |
| NEICA0371157 | 34.04994 | -118.231 | LA CO., METROPOLITAN TRANS AUT | CHATSWORTH, CA | MC, TCA | 30.8 | 384.2 |  |  |  |  |
| NEICA0371160 | 33.87859 | -118.0227 | HAYES - LEMMERZ INTERNATIONAL | LA MIRADA, CA | MC | 1897.8 |  |  |  |  |  |
| NEICA0371195 | 34.14991 | -118.3211 | THE WALT DISNEY COMPANY | BURBANK, CA | TCA, TCE |  | 1088.1 |  | 81.7 |  |  |
| NEICA0371208 | 33.81791 | -118.1841 | TRICO INDUSTRIES INC | SIGNAL HILL, CA | TCA, PCE |  | 2254.9 | 59.4 |  |  |  |
| NEICA0371215 | 33.94823 | -118.0679 | REDI STRIP CO | SANTA FE SPRINGS, CA | MC | 1098.6 |  |  |  |  |  |
| NEICA0371221 | 34.22259 | -118.4941 | KAL GARD COATING & MFG CORP | SEPULVEDA, CA | TCA |  | 11094.0 |  |  |  |  |
| NEICA0371232 | 34.00996 | -118.4411 | MARCONI ASTRONICS INC | SANTA MONICA, CA | TCA |  | 9973.4 |  |  |  |  |
| NEICA0371235 | 34.14442 | -118.7898 | TERADYNE INC | AGOURA HILLS, CA | TCA |  | 368.8 |  |  |  |  |
| NEICA0371243 | 33.82586 | -118.3157 | M/A-COM, A DIVN. OF AMP INC. | TORRANCE, CA | TCA |  | 1367.2 |  |  |  |  |
| NEICA0371244 | 34.21598 | -118.5951 | CONDOR PACIFIC IND INC | CANOGA PARK, CA | MC, TCA | 1148.3 | 639.9 |  |  |  |  |
| NEICA0371271 | 33.99999 | -118.221 | CONSOLIDATED FABRICATORS CORP | VERNON, CA | TCA |  | 536.6 |  |  |  |  |
| NEICA0371308 | 34.04994 | -118.231 | LA CO., METROPOLITAN TRANS AUT | LOS ANGELES, CA | MC, TCA | 41.7 | 469.9 |  |  |  |  |
| NEICA0371319 | 34.03999 | -118.1411 | SO CAL GAS CO | MONTEREY PARK, CA | MC, TCA | 0.4 | 0.4 |  |  |  |  |
| NEICA0371331 | 34.375 | -118.019 | WAMBOLD FURNITURE | SIMI VALLEY, CA | TCA |  | 549.8 |  |  |  |  |
| NEICA0371347 | 33.99877 | -118.3132 | LA CO., METROPOLITAN TRANS AUT | LOS ANGELES, CA | MC, TCA | 32.7 | 356.5 |  |  |  |  |
| NEICA0371359 | 33.98993 | -117.891 | PUREX POOL SYSTEMS INC | INDUSTRY, CA | TCA |  | 13258.0 |  |  |  |  |
| NEICA0371361 | 33.9315 | -118.4094 | ALLIED-SIGNAL INC,GARRETT GEN | LOS ANGELES, CA | MC, TCA | 2547.0 | 56.2 |  |  |  |  |
| NEICA0371364 | 33.88233 | -118.0158 | QUEEN CARPET CORP, TUFTEX CARP | LA MIRADA, CA | MC | 342.9 |  |  |  |  |  |
| NEICA0371367 | 34.09151 | -118.0459 | THE VONS COMPANIES INC | EL MONTE, CA | TCA |  | 187.3 |  |  |  |  |
| NEICA0371372 | 34.17651 | -118.3051 | ALLIEDSIGNAL AEROSPACE, W COAS | BURBANK, CA | MC, TCA | 189.2 | 979.1 |  |  |  |  |
| NEICA0371378 | 33.99712 | -118.2104 | BARKSDALE INC | LOS ANGELES, CA | MC, TCA, TCE | 277.7 | 1417.0 |  | 313.0 |  |  |
| NEICA0371384 | 34.03996 | -118.6911 | HRL LABORATORIES, LLC | MALIBU, CA | MC, TCA, PCE, Chloroform | 22.1 | 17.5 | 111.2 |  |  | 5.5 |
| NEICA0371392 | 33.85966 | -118.1565 | SULLY-MILLER CONTRACTING CO,BL | LONG BEACH, CA | PCE |  |  | 95.3 |  |  |  |
| NEICA0371477 | 33.80992 | -118.3311 | CUSHION CUT INC | TORRANCE, CA | TCA |  | 5687.1 |  |  |  |  |
| NEICA0371478 | 34.18388 | -118.5971 | DATA PROD. CORP | WOODLAND HILLS, CA | TCA |  | 147.0 |  |  |  |  |
| NEICA0371497 | 34.29997 | -118.4711 | BEI SYSTRON DONNER CO, EDCLIFF | SYLMAR, CA | TCA |  | 1770.6 |  |  |  |  |
| NEICA0371508 | 34.19065 | -118.5974 | THE BOEING COMPANY | CANOGA PARK, CA | TCA, PCE |  | 11.8 | 36.5 |  |  |  |
| NEICA0371525 | 34.00898 | -118.2358 | BENDER MACHINE INC | LOS ANGELES, CA | TCA |  | 105.7 |  |  |  |  |
| NEICA0371551 | 33.8968 | -118.0359 | TUFTEX CARPET MILLS INC,LA MIR | SANTA FE SPRINGS, CA | MC | 342.9 |  |  |  |  |  |
| NEICA0371587 | 33.91996 | -118.1311 | THE BOEING COMPANY | DOWNEY, CA | TCA |  | 10426.7 |  |  |  |  |
| NEICA0371606 | 33.9299 | -118.3901 | BOEING SATELLITE SYSTEMS INC | EL SEGUNDO, CA | MC, TCA | 5.1 | 0.0 |  |  |  |  |
| NEICA0378 | 34.11993 | -117.9211 | PERKINELMER OPTOELECTRONICS SC | AZUSA, CA | MC, TCA | 12797.2 | 28183.5 |  |  |  |  |
| NEICA0379995 | 34.42993 | -118.5711 | HR TEXTRON INC. | PACOIMA, CA | TCA |  | 6743.6 |  |  |  |  |
| NEICA0379999 | 34.42993 | -118.5711 | HR TEXTRON INC | VALENCIA, CA | TCA |  | 13252.8 |  |  |  |  |
| NEICA05920 | 33.65114 | -117.8668 | CONEXANT SYSTEMS INC | NEWPORT BEACH, CA | TCA |  | 277.6 |  |  |  |  |
| NEICA0592016 | 33.70997 | -117.841 | TROY SYSTEMS INC | SANTA ANA, CA | TCA |  | 2173.8 |  |  |  |  |
| NEICA0592024 | 33.71963 | -117.8524 | MARK OPTICS INC. | SANTA ANA, CA | TCA |  | 3353.0 |  |  |  |  |
| NEICA0592045 | 33.70318 | -117.9972 | REVCO PRODUCTS INC | HUNTINGTON BEACH, CA | TCA |  | 136.4 |  |  |  |  |
| NEICA0592046 | 33.70685 | -117.908 | ROI DEVELOPMENT CORP | SANTA ANA, CA | TCA |  | 988.8 |  |  |  |  |
| NEICA0592051 | 33.72025 | -117.9113 | SUPERIOR MANUFACTURING CO | SANTA ANA, CA | TCA |  | 2439.4 |  |  |  |  |
| NEICA0592053 | 33.69998 | -117.8511 | 3M MEDICAL PRODUCTS | IRVINE, CA | MC, TCA | 4100.5 | 3224.1 |  |  |  |  |
| NEICA0592066 | 33.85901 | -117.8371 | ROTO-INDUSTRIES, INC | ANAHEIM, CA | MC, TCA | 2582.8 | 171.9 |  |  |  |  |
| NEICA0592069 | 33.91997 | -117.911 | IAC INDUSTRIES | BREA, CA | TCA |  | 9797.6 |  |  |  |  |
| NEICA0592070 | 33.85995 | -117.841 | THE BOEING COMPANY | ANAHEIM, CA | TCA |  | 13426.2 |  |  |  |  |
| NEICA0592075 | 33.80826 | -118.0557 | FURON COMPANY MECHANICAL SEAL | LOS ALAMITOS, CA | TCA |  | 789.2 |  |  |  |  |
| NEICA0592131 | 33.71996 | -117.831 | RICOH ELECTRONICS INC | IRVINE, CA | MC, PCE | 8878.2 |  | 13518.0 |  |  |  |
| NEICA0592137 | 33.85806 | -117.8895 | KIMBERLY-CLARK WORLDWIDE INC.- | FULLERTON, CA | TCA |  | 34182.3 |  |  |  |  |
| NEICA06029F0 | 34.92464 | -117.891 | EDWARDS AIR FORCE BASE | EDWARDS AFB, CA | MC, TCA, PCE, TCE, C Tetrachloride, Chloroform | 133.6 | 612.8 | 6.1 | 0.0 | 0.0 | 196.3 |
| NEICA0652160 | 33.91805 | -116.8548 | JACK STANFIELD CO INC, STANFIE | BANNING, CA | TCA |  | 2280.7 |  |  |  |  |
| NEICA0652166 | 33.49512 | -117.1542 | NATL PROCESS IND, INC | TEMECULA, CA | TCA |  | 302.1 |  |  |  |  |
| NEICA0652176 | 33.83045 | -117.2477 | PACIFIC WESTERN EXTRUDED PLAST | PERRIS, CA | TCA |  | 75.5 |  |  |  |  |
| NEICA0672219 | 38.51125 | -121.3736 | THE PALM IRON & BRIDGE WORKS | SACRAMENTO, CA | MC, TCA | 1769.0 | 1369.8 |  |  |  |  |
| NEICA0672435 | 38.51368 | -121.4728 | CAMPBELL SOUP COMPANY | SACRAMENTO, CA | MC | 836.3 |  |  |  |  |  |
| NEICA0712392 | 35.26521 | -116.6897 | US ARMY NATIONAL TRAINING CTR. | FORT IRWIN, CA | TCA, PCE |  | 30.8 | 30.8 |  |  |  |
| NEICA0712418 | 34.29797 | -114.2241 | MWD - GENE INTAKE PUMPING PLT. | PARKER DAM, CA | TCA |  | 1646.5 |  |  |  |  |
| NEICA0712460 | 34.04621 | -117.5315 | INLAND PAPERBOARD AND PACKAGIN | ONTARIO, CA | MC, PCE | 1588.5 |  | 3177.9 |  |  |  |
| NEICA0712464 | 34.04398 | -117.6132 | MAG INSTRUMENT INC | ONTARIO, CA | TCA |  | 14220.1 |  |  |  |  |
| NEICA0713037 | 38.0176 | -122.3531 | STEELSCAPE | RICHMOND, CA | TCA |  | 437.9 |  |  |  |  |
| NEICA0732551 | 32.88105 | -117.163 | COMPOSITE OPTICS INC | SAN DIEGO, CA | MC, TCA | 327.0 | 472.1 |  |  |  |  |
| NEICA0732603 | 32.63831 | -117.1075 | SOUTHBAY BOAT YARD | CHULA VISTA, CA | MC, TCA, PCE | 0.1 | 0.2 | 0.2 |  |  |  |
| NEICA0732639 | 32.81308 | -117.2184 | BKM INC. | SAN DIEGO, CA | TCA, PCE |  | 0.1 | 0.1 |  |  |  |
| NEICA0732675 | 33.13493 | -117.228 | KILLION INDUSTRIES | VISTA, CA | PCE |  |  | 613.3 |  |  |  |
| NEICA0732681 | 32.62924 | -117.1013 | ROHR INDUSTRIES. | CHULA VISTA, CA | MC, TCA, PCE, TCE | 2.4 | 2.4 | 2.4 | 463.5 |  |  |
| NEICA0732740 | 32.7022 | -117.1942 | USN NORTH ISLAND | SAN DIEGO, CA | MC, TCA, PCE | 8951.5 | 1.0 | 1.0 |  |  |  |
| NEICA0732742 | 32.65751 | -117.097 | PACORD INC. | NATIONAL CITY, CA | TCA, PCE |  | 0.1 | 0.1 |  |  |  |
| NEICA0732901 | 32.8085 | -116.9677 | STRIP SHOP THE | EL CAJON, CA | MC | 3392.9 |  |  |  |  |  |
| NEICA0732960 | 32.81696 | -116.9816 | CARPENTER SPECIAL PRODUCTS | EL CAJON, CA | PCE |  |  | 906.6 |  |  |  |
| NEICA0732967 | 33.21503 | -117.3979 | OCEANSIDE MARINE CENTRE, INC. | OCEANSIDE, CA | MC, TCA, PCE | 0.0 | 0.0 | 0.0 |  |  |  |
| NEICA0732968 | 32.6924 | -117.1395 | NORTH STAR PROPELLER, INC. | SAN DIEGO, CA | MC, TCA, PCE | 0.1 | 0.1 | 0.1 |  |  |  |
| NEICA0732973 | 33.10453 | -117.2163 | HUNTER INDUSTRIES | SAN MARCOS, CA | MC, TCA, PCE, TCE | 13.9 | 23.4 | 2.1 | 59.1 |  |  |
| NEICA0732981 | 32.82418 | -116.9912 | BUCK KNIVES, INC | EL CAJON, CA | PCE |  |  | 1194.1 |  |  |  |
| NEICA0733002 | 33.12518 | -117.2689 | GRAPHIC CONVERTING | CARLSBAD, CA | TCA |  | 94.8 |  |  |  |  |
| NEICA0733011 | 32.68971 | -117.1257 | PACIFIC SHIP REPAIR & FABRICAT | SAN DIEGO, CA | TCA, PCE |  | 0.2 | 0.4 |  |  |  |
| NEICA0733188 | 32.59324 | -117.0541 | MARINE SERVICE COMMERCIAL DIVI | CHULA VISTA, CA | MC, TCA, PCE | 0.0 | 0.0 | 0.0 |  |  |  |
| NEICA0733201 | 32.88001 | -117.1165 | USMC AIR STATION / MIRAMAR | SAN DIEGO, CA | MC, TCA, PCE | 4.1 | 6.9 | 6.9 |  |  |  |
| NEICA0733205 | 32.68244 | -117.1248 | USN 32ND ST NAV STATION | SAN DIEGO, CA | MC, TCA, PCE | 1.6 | 2.7 | 2.7 |  |  |  |
| NEICA0733211 | 32.67162 | -117.1694 | USN AMPHIBIOUS BASE | CORONADO, CA | MC, TCA, PCE | 1.2 | 2.0 | 2.0 |  |  |  |
| NEICA0733419 | 32.70036 | -117.242 | USN SUBMARINE BASE | SAN DIEGO, CA | MC, TCA, PCE | 0.0 | 0.0 | 0.0 |  |  |  |
| NEICA0733422 | 32.84578 | -116.9711 | RCP BLOCK & BRICK | SANTEE, CA | MC, TCA, PCE | 0.0 | 0.0 | 0.0 |  |  |  |
| NEICA0733441 | 32.7754 | -117.0726 | S. D. STATE UNIVERSITY | SAN DIEGO, CA | MC, PCE | 6.0 |  | 14.6 |  |  |  |
| NEICA0773887 | 37.72168 | -121.4988 | TRACY OPERATORS | TRACY, CA | PCE |  |  | 0.1 |  |  |  |
| NEICA0834298 | 34.43709 | -119.8438 | INNOVATIVE MICRO TECHNOLOGY, INC. (IMT) | GOLETA, CA | TCA, PCE, TCE |  | 259.5 | 259.5 | 259.5 |  |  |
| NEICA0834316 | 34.59887 | -120.4603 | CELITE CORPORATION | LOMPOC, CA | TCA, PCE, TCE |  | 49.0 | 49.0 | 49.0 |  |  |
| NEICA0834319 | 34.38906 | -119.4832 | MCGHAN MEDICAL - 1160 MARK AVENUE | CARPINTERIA, CA | TCA, PCE, TCE |  | 74.4 | 74.4 | 74.4 |  |  |
| NEICA0834320 | 34.48421 | -120.0403 | EXXON - SYU PROJECT | GOLETA, CA | PCE |  |  | 8.2 |  |  |  |
| NEICA0838003 | 34.691 | -120.037 | NUEVO - SOUTH COUNTY OFFSHORE | OCEAN SHELF, CA | PCE |  |  | 1383.5 |  |  |  |
| NEICA0838009 | 34.43032 | -119.8664 | EXXON - SYU PROJECT | GOLETA, CA | PCE |  |  | 67.1 |  |  |  |
| NEICA0838012 | 34.691 | -120.037 | NUEVO - PLATFORM HABITAT | OCEAN SHELF, CA | PCE |  |  | 113.4 |  |  |  |
| NEICA0838013 | 34.43032 | -119.8664 | THE POINT ARGUELLO PROJECT | SB COUNTY, CA | PCE |  |  | 117.9 |  |  |  |
| NEICA0838016 | 34.72453 | -120.4346 | NUEVO - LOMPOC/PT. PED | LOMPOC, CA | TCA, PCE, TCE |  | 408.2 | 430.9 | 408.2 |  |  |
| NEICA0838999 | 34.01386 | -119.7456 | THE JET CENTER @ SANTA BARBARA | SANTA CRUZ ISLAND, CA | TCA, PCE, TCE |  | 274.0 | 274.0 | 274.0 |  |  |
| NEICA0854523 | 37.40929 | -122.0349 | LOCKHEED MARTIN CORPORATION | SUNNYVALE, CA | TCA |  | 21.4 |  |  |  |  |
| NEICA0854614 | 37.45204 | -122.125 | SARONIX | PALO ALTO, CA | TCA |  | 167.3 |  |  |  |  |
| NEICA0854766 | 37.40731 | -122.1507 | LOCKHEED MARTIN CORPORATION, M | PALO ALTO, CA | TCA |  | 39.9 |  |  |  |  |
| NEICA0854805 | 37.3755 | -121.9202 | PIERCEY TOYOTA, INC | SAN JOSE, CA | MC | 55.2 |  |  |  |  |  |
| NEICA0854846 | 37.38782 | -121.9065 | SANMINA CORPORATION | SAN JOSE, CA | MC | 2213.8 |  |  |  |  |  |
| NEICA0854854 | 37.37426 | -121.962 | SEMTECH SANTA CLARA | SANTA CLARA, CA | TCA |  | 15.2 |  |  |  |  |
| NEICA0854877 | 37.3968 | -122.1561 | AGILENT TECHNOLOGIES, INC | PALO ALTO, CA | Chloroform |  |  |  |  |  | 1.7 |
| NEICA0854911 | 37.39338 | -121.9334 | INTERNATIONAL MICROELECTRONICS | SAN JOSE, CA | TCA |  | 3.8 |  |  |  |  |
| NEICA0955098 | 38.27206 | -121.9878 | R & M ENERGY SYSTEMS | FAIRFIELD, CA | TCE |  |  |  | 1508.3 |  |  |
| NEICA1014302 | 36.51389 | -119.552 | SILGAN CONTAINERS MANUFAC CORP | KINGSBURG, CA | MC, TCA, PCE | 0.7 | 0.7 | 0.7 |  |  |  |
| NEICA10538 | 35.34379 | -118.7293 | CALIFORNIA CRRCTNL INST-THCHP | TEHACHAPI, CA | TCA |  | 4.6 |  |  |  |  |
| NEICA10782 | 33.777 | -115.91 | MORENO VALLEY SCH DIST | SUNNYMEAD, CA | TCA |  | 0.2 |  |  |  |  |
| NEICA1114712 | 34.2697 | -118.7187 | ROYAL COATINGS | SIMI VALLEY, CA | MC, TCA, PCE, TCE | 11.6 | 1152.0 | 97.8 | 11.6 |  |  |
| NEICA1115531 | 34.11037 | -119.1054 | NAVAL BASE VENTURA COUNTY | POINT MUGU, CA | MC, TCA | 100.1 | 28.3 |  |  |  |  |
| NEICA1115591 | 34.18903 | -118.9293 | TELEDYNE ELECTRONICS | NEWBURY PARK, CA | TCA |  | 1509.6 |  |  |  |  |
| NEICA1115634 | 34.23277 | -119.0128 | OPTIMUM OPTICAL SYSTEMS INC | CAMARILLO, CA | TCA |  | 431.3 |  |  |  |  |
| NEICA1115663 | 34.32938 | -119.0042 | VINTAGE OMN FIRST JOINT VENTU | SANTA PAULA, CA | TCA, PCE |  | 2.2 | 2.2 |  |  |  |
| NEICA1115684 | 34.21627 | -119.0287 | EVEREST & JENNINGS INC | CAMARILLO CA, CA | TCA |  | 2370.0 |  |  |  |  |
| NEICA1115685 | 34.20629 | -119.0328 | AIR COOLING TECHNOLOGY | CAMARILLO, CA | TCA |  | 2742.0 |  |  |  |  |
| NEICA1115692 | 34.27148 | -118.7207 | ENDERLE FUEL INJECTION | SIMI VALLEY, CA | TCA, PCE |  | 178.8 | 3.3 |  |  |  |
| NEICA1115697 | 34.27863 | -118.9074 | TENCAL INC. | SIMI VALLEY, CA | TCA, PCE |  | 0.1 | 0.1 |  |  |  |
| NEICA1115704 | 34.22359 | -119.0223 | TRANSCO PRODUCTS INC. | CAMARILLO, CA | TCA, Chloroform |  | 1097.7 |  |  |  | 1771.1 |
| NEICA1115736 | 34.25701 | -119.2273 | SANTA BARBARA APPLIED OPTICS | VENTURA, CA | TCA |  | 678.6 |  |  |  |  |
| NEICA2611601 | 34.19997 | -118.4411 | LA CITY, DWP | VAN NUYS, CA | TCA |  | 553.8 |  |  |  |  |
| NEICA3116233 | 38.77976 | -121.3088 | NEC ELECTRONICS INC | ROSEVILLE, CA | TCA |  | 1059.7 |  |  |  |  |
| NEICAT$12739 | 34.15 | -118.2711 | PRC-DE SOTO INTERNATIONAL | GLENDALE, CA | TCA |  | 71722.9 |  |  |  |  |
| NEICAT$12841 | 32.81472 | -116.9515 | KETEMA / A & E DIVISION | EL CAJON, CA | TCA |  | 548.8 |  |  |  |  |
| NEICO0048 | 38.23155 | -104.6122 | CF&I STEEL L P DBA ROCKY MTN STEEL MILLS | PUEBLO, CO | PCE |  |  | 37.2 |  |  |  |
| NEICO0050996 | 39.62186 | -104.9878 | BURT CHEVROLET | ENGLEWOOD, CO | MC | 51.8 |  |  |  |  |  |
| NEICO0310511 | 39.70921 | -104.9911 | TOOLS FOR BENDING INC | DENVER, CO | PCE |  |  | 338.6 |  |  |  |
| NEICO0623 | 39.80507 | -104.9783 | CHART STORAGE SYSTEMS - DENVER, INC | DENVER, CO | TCE |  |  |  | 603.3 |  |  |
| NEICO0632 | 40.13913 | -105.1274 | PCC COMPOSITES.CN | LONGMONT, CO | TCE |  |  |  | 453.6 |  |  |
| NEICO1768 | 39.68337 | -104.9898 | RJR CIRCUITS INC | DENVER, CO | MC | 58.5 |  |  |  |  |  |
| NEICTT$622 | 41.29123 | -72.92282 | SARGENT MANUFACTURING CO. | NEW HAVEN, CT | TCE |  |  |  | 3574.3 |  |  |
| NEIFL0250677 | 25.80638 | -80.29302 | SONIC AVIATION | MIAMI, FL | MC | 1551.3 |  |  |  |  |  |
| NEIFL1010335 | 28.2758 | -82.62377 | PALL AEROPOWER CORP | NEW PORT RICHEY, FL | TCE |  |  |  | 290.3 |  |  |
| NEIFL1030098 | 27.81557 | -82.75118 | ESSILOR OF AMERICA, INC. | ST PETERSBURG, FL | MC | 469.8 |  |  |  |  |  |
| NEIFL1030416 | 27.8697 | -82.71741 | FLORIDA METAL STAMPING INC | LARGO, FL | TCE |  |  |  | 5157.9 |  |  |
| NEIFL1030447 | 27.87529 | -82.73253 | RAYTHEON COMPANY | LARGO, FL | MC | 680.4 |  |  |  |  |  |
| NEIFLR023003 | 30.17481 | -82.5754 | TIMCO | LAKE CITY, FL | MC | 10.9 |  |  |  |  |  |
| NEIFLR083013 | 29.21804 | -82.14309 | MICKEY BODY COMPANY | OCALA, FL | MC | 9.1 |  |  |  |  |  |
| NEIIAES0713f | 40.42259 | -91.41224 | METSO MINERALS INDUSTRIES, INC. | KEOKUK, IA | PCE |  |  | 3601.5 |  |  |  |
| NEIIART$7942 | 41.71749 | -93.04318 | MAYTAG - NEWTON LAUNDRY PRODUCTS - PLANT 2 | NEWTON, IA | MC | 0.0 |  |  |  |  |  |
| NEIIAT$7932 | 41.41369 | -95.03408 | GLACIER DAIDO AMERICA, LLC | ATLANTIC, IA | PCE, TCE |  |  | 17887.1 | 2086.9 |  |  |
| NEIIAT$8120 | 40.63164 | -91.30244 | SHEAFFER MANUFACTURING CO., LLC | FORT MADISON, IA | TCE |  |  |  | 298.9 |  |  |
| NEIIL0075859 | 42.251 | -88.876 | M & R RUBBER CO | BELVIDERE, IL | PCE |  |  | 244.9 |  |  |  |
| NEIIL0115886 | 41.3875 | -89.4572 | HARPER WYMAN CO | PRINCETON, IL | TCE |  |  |  | 16743.0 |  |  |
| NEIIL031195A | 42.02662 | -87.78644 | JOHN CRANE INC | MORTON GROVE, IL | TCE |  |  |  | 15240.7 |  |  |
| NEIIL03142 | 42.019 | -87.793 | OAKLEY INDUSTRIES INC | NILES, IL | TCE |  |  |  | 5588.3 |  |  |
| NEIIL0316063 | 41.4985 | -87.682 | HOLLYMATIC CORP | COUNTRYSIDE, IL | PCE |  |  | 4350.9 |  |  |  |
| NEIIL0316147 | 41.9411 | -87.8564 | BRUNNER AND LAY INC | FRANKLIN PARK, IL | PCE |  |  | 147.4 |  |  |  |
| NEIIL0316332 | 41.855 | -87.8576 | ECS CORP | BROADVIEW, IL | TCE |  |  |  | 1415.2 |  |  |
| NEIIL0316389 | 41.8751 | -87.8675 | HA FRAMBURG AND CO | BELLWOOD, IL | TCE |  |  |  | 3728.5 |  |  |
| NEIIL0316435 | 42.011 | -87.721 | RF MAU CO | LINCOLNWOOD, IL | MC | 8605.6 |  |  |  |  |  |
| NEIIL0316467 | 42.0397 | -87.7936 | DIEBEL MANUFACTURING CO | MORTON GROVE, IL | TCE |  |  |  | 11887.7 |  |  |
| NEIIL0316542 | 41.8193 | -87.863 | MUSSER DIVISION-SELMER CO INC | LAGRANGE, IL | MC | 2194.7 |  |  |  |  |  |
| NEIIL0316594 | 41.9497 | -87.8636 | MJ CELCO | SCHILLER PARK, IL | TCE |  |  |  | 13338.3 |  |  |
| NEIIL0316639 | 42.026 | -87.715 | RAULAND-BORG CORP | SKOKIE, IL | TCE |  |  |  | 3954.4 |  |  |
| NEIIL0316641 | 42.0188 | -87.7189 | OHMITE MANUFACTURING CO | SKOKIE, IL | TCE |  |  |  | 1651.1 |  |  |
| NEIIL0316678 | 42.1481 | -87.8689 | NATIONAL COATING TECHNOLOGIES | NORTHBROOK, IL | TCA |  | 1332.4 |  |  |  |  |
| NEIIL0316686 | 42.1456 | -87.8531 | RAMCEL ENGINEERING CO | NORTHBROOK, IL | MC | 6531.7 |  |  |  |  |  |
| NEIIL0316702 | 42.0189 | -87.7852 | SYNCHRO-START PRODUCTS INC | NILES, IL | TCE |  |  |  | 471.7 |  |  |
| NEIIL0316720 | 42.019 | -87.781 | DRAWN METAL PRODUCTS DIVISION | NILES, IL | TCE |  |  |  | 1567.6 |  |  |
| NEIIL0316721 | 42.016 | -87.782 | SATE-LITE MANUFACTURING CO | NILES, IL | TCE |  |  |  | 170.5 |  |  |
| NEIIL0316723 | 42.0121 | -87.7852 | AB DICK CO | NILES, IL | PCE |  |  | 530.7 |  |  |  |
| NEIIL0316747 | 41.9335 | -87.8496 | FORT LOCK CORP | RIVER GROVE, IL | TCE |  |  |  | 181.4 |  |  |
| NEIIL0316842 | 42.0031 | -88.0075 | LIGHTNING METAL SPECIALTY | ELK GROVE VILLAGE, IL | TCE |  |  |  | 235.9 |  |  |
| NEIIL0316995 | 41.8839 | -87.6494 | CHICAGO-ALLIS MFG CORP | CHICAGO, IL | PCE |  |  | 2.3 |  |  |  |
| NEIIL0317010 | 41.9386 | -87.7131 | P & H PLATING CO INC | CHICAGO, IL | TCE |  |  |  | 4981.5 |  |  |
| NEIIL0317020 | 41.8072 | -87.6992 | CENTRAL DIE CASTING | CHICAGO, IL | PCE |  |  | 9162.7 |  |  |  |
| NEIIL0317093 | 41.8156 | -87.714 | YALE POLISHING & PLATING | CHICAGO, IL | TCE |  |  |  | 2176.9 |  |  |
| NEIIL0317139 | 41.8878 | -87.6673 | NOBERT PLATING CO | CHICAGO, IL | TCE |  |  |  | 1943.8 |  |  |
| NEIIL0317140 | 41.8803 | -87.6575 | BARNES PLATING CORP | CHICAGO, IL | TCE |  |  |  | 320.8 |  |  |
| NEIIL0317197 | 41.9297 | -87.6753 | PLASTICS CAPACITORS INC PLANT 2 | CHICAGO, IL | TCE |  |  |  | 2000.3 |  |  |
| NEIIL0317202 | 41.9594 | -87.6744 | WM. E. WRIGHT CO | CHICAGO, IL | TCE |  |  |  | 48.5 |  |  |
| NEIIL0317366 | 41.81571 | -87.72155 | BAGCRAFT PACKAGING LLC | CHICAGO, IL | PCE |  |  | 2171.2 |  |  |  |
| NEIIL0317662 | 41.915 | -87.739 | MILTON INDUSTRIES INC | CHICAGO, IL | TCE |  |  |  | 725.7 |  |  |
| NEIIL0317669 | 41.939 | -87.688 | BULAW WELDING | CHICAGO, IL | TCE |  |  |  | 3453.1 |  |  |
| NEIIL0317689 | 41.9814 | -87.7605 | RS OWENS AND CO | CHICAGO, IL | TCE |  |  |  | 4037.0 |  |  |
| NEIIL043020A | 41.90546 | -88.1027 | METALS TECHNOLOGY CORP | CAROL STREAM, IL | TCE |  |  |  | 13557.7 |  |  |
| NEIIL043095A | 41.8 | -87.9667 | AMERICAN COUPLINGS CO | WESTMONT, IL | TCE |  |  |  | 5965.6 |  |  |
| NEIIL0435ALQ | 41.9238 | -87.9911 | DIAL TOOL CO | ADDISON, IL | TCE |  |  |  | 4045.1 |  |  |
| NEIIL0437946 | 41.9251 | -88.0852 | DUPAGE MACHINE | GLENDALE HEIGHTS, IL | MC | 6119.9 |  |  |  |  |  |
| NEIIL0438058 | 41.8 | -88.0417 | TRICON IND | DOWNERS GROVE, IL | PCE |  |  | 158.7 |  |  |  |
| NEIIL0438068 | 41.79488 | -88.0434 | REXNORD CORP - REX BEARING DIV | DOWNERS GROVE, IL | TCE |  |  |  | 1168.0 |  |  |
| NEIIL0438080 | 41.977 | -87.987 | DE AMERTEK CORPORATION INC | OAK BROOK, IL | TCE |  |  |  | 88.5 |  |  |
| NEIIL0438118 | 41.9711 | -87.9425 | LD REDMER SCREW PRODUCTS INC | BENSENVILLE, IL | TCE |  |  |  | 934.4 |  |  |
| NEIIL0458147 | 39.5989 | -87.6936 | MECO INC | PARIS, IL | PCE |  |  | 8972.4 |  |  |  |
| NEIIL0638273 | 41.3833 | -88.4167 | BIMET CORP | MORRIS, IL | PCE |  |  | 7170.4 |  |  |  |
| NEIIL0738305 | 41.44751 | -90.16134 | SPRINGFIELD INC | GENESEO, IL | TCA |  | 1564.9 |  |  |  |  |
| NEIIL089080A | 41.996 | -88.293 | HEAD INC | SOUTH ELGIN, IL | TCE |  |  |  | 3265.9 |  |  |
| NEIIL0898477 | 42.073 | -88.296 | WAUCONDA TOOL & ENGINEERING CO INC | ELGIN, IL | TCE |  |  |  | 907.2 |  |  |
| NEIIL0898484 | 41.9158 | -88.3185 | MET-CO INDUSTRIES | ST. CHARLES, IL | TCA |  | 1527.2 |  |  |  |  |
| NEIIL0978631 | 42.1928 | -88.1167 | CM PRODUCTS INC | LAKE ZURICH, IL | TCE |  |  |  | 8853.9 |  |  |
| NEIIL0978727 | 42.259 | -87.987 | PERFORMANCE LASER & FAB | MUNDELEIN, IL | TCE |  |  |  | 3401.9 |  |  |
| NEIIL0978767 | 42.2729 | -87.9054 | PETCO INC | LAKE FOREST, IL | MC | 7068.8 |  |  |  |  |  |
| NEIIL0998825 | 41.1269 | -88.7981 | TELEWELD INC | STREATOR, IL | TCE |  |  |  | 175.9 |  |  |
| NEIIL111005A | 42.1703 | -88.2989 | WAUCONDA TOOL & ENGINEERING | ALGONQUIN, IL | TCE |  |  |  | 3776.6 |  |  |
| NEIIL1110AAD | 42.4697 | -88.4348 | KEYSTONE DISPLAY INC | HEBRON, IL | TCE |  |  |  | 2812.3 |  |  |
| NEIIL1118956 | 42.4806 | -88.3092 | CLAUD S GORDON CO | RICHMOND, IL | TCE |  |  |  | 1714.1 |  |  |
| NEIIL1118985 | 42.1992 | -88.233 | DUREX INTERNATIONAL CORP | CARY, IL | PCE |  |  | 1348.0 |  |  |  |
| NEIIL1118996 | 42.2502 | -88.3091 | PRECISION TWIST DRILL CO | CRYSTAL LAKE, IL | TCE |  |  |  | 2722.3 |  |  |
| NEIIL1118998 | 42.2447 | -88.3073 | AUTOTROL CORP | CRYSTAL LAKE, IL | TCE |  |  |  | 1611.2 |  |  |
| NEIIL1119000 | 42.2083 | -88.2575 | ELECPAC DIV | CARY, IL | TCA |  | 849.1 |  |  |  |  |
| NEIIL1119043 | 42.2378 | -88.315 | G & M MFG CORP | CRYSTAL LAKE, IL | MC | 7642.1 |  |  |  |  |  |
| NEIIL18396 | 40.1403 | -87.584 | VERMILION RUBBER TECHNOLOGY INC | DANVILLE, IL | TCE |  |  |  | 747.2 |  |  |
| NEIIL1839883 | 40.1267 | -87.6453 | THERMO TECHNIQUES | DANVILLE, IL | TCE |  |  |  | 5080.2 |  |  |
| NEIIL1839900 | 40.1275 | -87.6442 | DANVILLE METAL STAMPING CO | DANVILLE, IL | TCE |  |  |  | 6985.2 |  |  |
| NEIIL2010AZW | 42.2617 | -89.0953 | BARRON INDUSTRIES | ROCKFORD, IL | TCE |  |  |  | 4176.6 |  |  |
| NEIIL227 | 42.45755 | -89.05691 | WOODWARD GOVERNOR CO | ROCKTON, IL | MC | 148.6 |  |  |  |  |  |
| NEIIL241 | 42.2191 | -89.0249 | CHEM PROCESSING INC | ROCKFORD, IL | TCE |  |  |  | 4898.8 |  |  |
| NEIIL323 | 42.4561 | -89.0395 | REGAL-BELOIT CORP | SOUTH BELOIT, IL | TCA |  | 1386.9 |  |  |  |  |
| NEIIL91 | 41.4428 | -88.2022 | METALSTAMP INC | CHANNAHON, IL | TCE |  |  |  | 2517.4 |  |  |
| NEIILT$9050 | 42.04618 | -87.99005 | BUHRKE INDUSTRIES INC | ARLINGTON HEIGHTS, IL | TCE |  |  |  | 29.0 |  |  |
| NEIILT$9130 | 42.0264 | -87.7113 | GENERAL AUTOMATION INC | SKOKIE, IL | TCE |  |  |  | 5454.0 |  |  |
| NEIILT$9235 | 41.9467 | -88.3955 | CARDINAL INDUSTRIES | ST. CHARLES, IL | MC | 7861.2 |  |  |  |  |  |
| NEIIN0010001 | 40.82 | -84.94 | GILPIN IRONWORKS INC. | DECATUR, IN | TCE |  |  |  | 26551.5 |  |  |
| NEIIN00119 | 39.89008 | -86.06086 | BEST ACCESS SYSTEMS | INDIANAPOLIS, IN | MC, TCE | 81.0 |  |  | 1.6 |  |  |
| NEIIN00247 | 41.6189 | -87.52472 | VERMETTE MACHINE CO., INC. | HAMMOND, IN | TCE |  |  |  | 1892.0 |  |  |
| NEIIN00297 | 39.7688 | -86.11163 | CMW, INC. | INDIANAPOLIS, IN | TCE |  |  |  | 6852.9 |  |  |
| NEIIN0390015 | 41.69222 | -85.99417 | EK BLESSINGS COMPANY, INC. | ELKHART, IN | TCE |  |  |  | 4273.7 |  |  |
| NEIIN039144 | 41.70023 | -85.99653 | CONN-SELMER, INC., VINCENT BACH DIVISION | ELKHART, IN | TCE |  |  |  | 1415.7 |  |  |
| NEIIN051153 | 38.33642 | -87.3399 | BRIDON-AMERICAN CORP. | OAKLAND CITY, IN | TCE |  |  |  | 1628.8 |  |  |
| NEIIN0890254 | 41.60817 | -87.47402 | VIKING ENGINEERING COMPANY, INC. | HAMMOND, IN | TCE |  |  |  | 71.7 |  |  |
| NEIIN555 | 41.35333 | -86.33361 | WHITLEY PRODUCTS, INC | PLYMOUTH, IN | TCE |  |  |  | 4082.3 |  |  |
| NEIKS00075 | 37.65028 | -97.26972 | CESSNA AIRCRAFT CO.-PAWNEE FACILITY | WICHITA, KS | MC, TCE | 235.9 |  |  | 26308.4 |  |  |
| NEIKS00165 | 37.66667 | -97.37639 | GLOBE ENGINEERING COMPANY, INC. | WICHITA, KS | TCE |  |  |  | 7085.1 |  |  |
| NEIKS325 | 37.04417 | -95.62334 | CLEAN HARBORS COFFEYVILLE, LLC | COFFEYVILLE, KS | PCE |  |  | 53986.6 |  |  |  |
| NEIKST$10304 | 37.665 | -97.42805 | LEARJET, INC. | WICHITA, KS | TCE |  |  |  | 3884.2 |  |  |
| NEIKST$10326 | 37.64722 | -97.4075 | CESSNA AIRCRAFT DIVISION - MID-CONTINENT | WICHITA, KS | MC, TCE | 335.7 |  |  | 6767.6 |  |  |
| NEIKY009210 | 36.99232 | -85.95199 | AMAK BRAKE LLC | GLASGOW, KY | TCE |  |  |  | 771.1 |  |  |
| NEIKY1131 | 36.96972 | -86.47527 | PARTS CLEANING TECHNOLOGIES | BOWLING GREEN, KY | TCE |  |  |  | 42067.5 |  |  |
| NEIKY1145 | 38.06503 | -84.72253 | YH AMERICA INCORPORATED | VERSAILLES, KY | TCA, PCE |  | 3666.7 | 91.4 |  |  |  |
| NEIKY719 | 38.06163 | -84.92781 | GENERAL CABLE COMPANY | LAWRENCEBURG, KY | TCE |  |  |  | 13281.2 |  |  |
| NEIKY793 | 37.98724 | -84.17041 | COSMO WHEELS INC | WINCHESTER, KY | TCA |  | 272.2 |  |  |  |  |
| NEIKY829 | 38.04365 | -84.47022 | CENTRAL KY PROCESS | LEXINGTON, KY | TCE |  |  |  | 898.1 |  |  |
| NEIKY909 | 37.80779 | -87.64065 | GIBBS DIE CASTING ALUMIN | HENDERSON, KY | TCA |  | 13374.5 |  |  |  |  |
| NEIKY917 | 37.8049 | -87.64093 | GIBBS DIE CASTING ALUMINM | HENDERSON, KY | TCA |  | 10.8 |  |  |  |  |
| NEIKY987 | 36.84945 | -86.9 | J S TECHNOS CORPORATION | RUSSELLVILLE, KY | TCE |  |  |  | 4550.4 |  |  |
| NEIKYT$5489 | 38.07924 | -84.53398 | BOSCH REXROTH CORPORATION | LEXINGTON, KY | TCE |  |  |  | 2375.7 |  |  |
| NEILA1150010 | 31.04856 | -93.20852 | JRTC & FT POLK/FT POLK | FT. POLK, LA | MC, TCA, PCE | 7.7 | 1.4 | 1.4 |  |  |  |
| NEIMI027N588 | 41.79798 | -86.05157 | MERCURY DISPLACEMENT INDUSTRIES | EDWARDSBURG, MI | MC | 23.1 |  |  |  |  |  |
| NEIMI049N112 | 43.13438 | -83.71715 | UNIVERSAL COATING INC | MOUNT MORRIS, MI | TCE |  |  |  | 291.1 |  |  |
| NEIMI065A163 | 42.67694 | -84.52947 | PRATT & WHITNEY AUTOAIR | LANSING, MI | TCE |  |  |  | 1826.2 |  |  |
| NEIMI161N505 | 42.22826 | -83.69166 | SCP ENTERPRISES INC | ANN ARBOR, MI | MC | 261.5 |  |  |  |  |  |
| NEIMI163A895 | 42.37123 | -83.35366 | KOPACZ INDUSTRIAL PAINTING CO | LIVONIA, MI | TCE |  |  |  | 856.9 |  |  |
| NEIMI163N024 | 42.29102 | -83.29026 | AMETEK PRESTOLITE MOTORS | DEARBORN HTS, MI | TCE |  |  |  | 999.7 |  |  |
| NEIMI2612119 | 43.25101 | -86.21952 | GENERAL DYNAMICS LAND SYSTEMS MUSKEGON | MUSKEGON, MI | TCA |  | 561.3 |  |  |  |  |
| NEIMIA0155 | 42.64195 | -85.30884 | HASTINGS FIBERGLASS PRODUCTS INC | HASTINGS, MI | MC | 24.9 |  |  |  |  |  |
| NEIMIA2416 | 42.89452 | -85.54861 | STEPHENSON AND LAWYER INC | GRAND RAPIDS, MI | MC | 3312.0 |  |  |  |  |  |
| NEIMIA2447 | 42.91099 | -85.67379 | INTERNAL GRINDING ABRASIVE | GRAND RAPIDS, MI | MC, PCE | 0.5 |  | 478.1 |  |  |  |
| NEIMIA2931 | 42.60276 | -83.93262 | DIAMOND CHROME PLATING INC | HOWELL, MI | TCE |  |  |  | 7184.9 |  |  |
| NEIMIB1904 | 43.22028 | -86.25697 | BRUNSWICK BOWLING AND BILLIARDS | MUSKEGON, MI | MC | 6085.7 |  |  |  |  |  |
| NEIMIB2289 | 41.89548 | -84.0172 | AGET MANUFACTURING CO | ADRIAN, MI | TCE |  |  |  | 4198.0 |  |  |
| NEIMIB4096 | 41.84806 | -85.65575 | OWENS ILLINOIS CLOSURE, INC. | CONSTANTINE, MI | TCE |  |  |  | 2257.8 |  |  |
| NEIMIB6220 | 42.59568 | -82.85286 | SELFRIDGE PLATING INC | HARRISON TWP, MI | TCE |  |  |  | 2934.7 |  |  |
| NEIMIB7018 | 42.48154 | -83.48188 | GENERAL FILTERS, INC. | NOVI, MI | TCE |  |  |  | 459.9 |  |  |
| NEIMIM4403 | 42.32849 | -83.41867 | DNR INC | WESTLAND, MI | TCE |  |  |  | 9887.4 |  |  |
| NEIMIM4607 | 42.19203 | -83.16755 | DETROIT TUBULAR RIVET INC | WYANDOTTE, MI | MC | 6593.9 |  |  |  |  |  |
| NEIMIN3303 | 42.30565 | -85.25904 | DUNCAN AVIATION INC. | BATTLE CREEK, MI | MC | 2144.6 |  |  |  |  |  |
| NEIMIN6173 | 45.29664 | -85.25023 | DME COMPANY | CHARLEVOIX, MI | PCE |  |  | 5.4 |  |  |  |
| NEIMIN6646 | 43.00068 | -84.20656 | OWOSSO GRAPHIC ARTS | OWOSSO, MI | TCE |  |  |  | 1798.0 |  |  |
| NEIMIN6660 | 42.51349 | -83.11049 | STANHOPE TOOL, INC. | MADISON HTS, MI | TCE |  |  |  | 304.4 |  |  |
| NEIMIT$7376 | 42.54959 | -82.94506 | SPECIALTY STEEL TREATING INC. | FRASER, MI | PCE |  |  | 1073.8 |  |  |  |
| NEIMIT$7475 | 41.92199 | -83.36831 | ADVANCED HEAT TREAT CORP | MONROE, MI | TCE |  |  |  | 5573.7 |  |  |
| NEIMN019264 | 44.841 | -93.5954 | MCLAUGHLIN GORMLEY KING CO - CHASKA | CHASKA, MN | MC | 6859.2 |  |  |  |  |  |
| NEIMN123294 | 44.9352 | -93.0757 | VIKING DRILL & TOOL INC | ST. PAUL, MN | TCE |  |  |  | 5059.4 |  |  |
| NEIMN1429 | 44.1732 | -94.0458 | MICO INC | NORTH MANKATO, MN | MC | 4941.9 |  |  |  |  |  |
| NEIMN2713900 | 44.7851 | -93.5084 | ADC TELECOMMUNICATIONS INC - SHAKOPEE | SHAKOPEE, MN | MC | 3871.9 |  |  |  |  |  |
| NEIMNT$8769 | 44.8278 | -93.2035 | FINISHING EQUIPMENT INC | EAGAN, MN | MC, TCE | 1187.2 |  |  | 3634.2 |  |  |
| NEIMNT$8791 | 44.8488 | -93.5946 | SUPER RADIATOR COILS - CHASKA | CHASKA, MN | PCE |  |  | 60154.5 |  |  |  |
| NEIMNT$8855 | 45.0834 | -93.3892 | THOMAS ENGINEERING CO | BROOKLYN PARK, MN | TCE |  |  |  | 4717.4 |  |  |
| NEIMNT$8860 | 45.1028 | -93.2662 | LARSEN'S MANUFACTURING CO | FRIDLEY, MN | TCE |  |  |  | 6362.5 |  |  |
| NEIMS025298 | 33.59163 | -88.64611 | BRYAN FOODS INC | WEST POINT, MS | PCE |  |  | 6.4 |  |  |  |
| NEINC0216 | 35.20867 | -80.94443 | US AIRWAYS, FOUR (4) SITE LOCATIONS | CHARLOTTE, NC | MC | 100.0 |  |  |  |  |  |
| NEINCT$3034 | 35.215 | -80.52444 | CORNING INCORPORATED | MIDLAND, NC | MC | 409.1 |  |  |  |  |  |
| NEINM0001 | 35.8598 | -106.3068 | LOS ALAMOS NATIONAL LABORATORY | LOS ALAMOS, NM | TCE |  |  |  | 9.1 |  |  |
| NEINM0031 | 32.27202 | -106.916 | METAL PARTS MFG | LAS CRUCES, NM | TCE |  |  |  | 11492.2 |  |  |
| NEINY1957 | 40.7 | -73.98 | BEN FORMAN & SONS INC | BROOKLYN, NY | TCE |  |  |  | 10777.4 |  |  |
| NEINY1998 | 43.08 | -75.25 | UTICA METAL PRODUCTS | UTICA, NY | TCE |  |  |  | 5303.4 |  |  |
| NEINY2054 | 40.92 | -73.86 | STEWART EFI NEW YORK LLC | YONKERS, NY | MC, TCE | 1095.4 |  |  | 567.9 |  |  |
| NEINY8265400 | 43.22 | -77.41 | XEROX JOSEPH C WILSON CTR FOR TECHNOLOGY | WEBSTER, NY | MC | 971.6 |  |  |  |  |  |
| NEIOH0351982 | 41.53235 | -81.54838 | MEYER PRODUCTS | CLEVELAND, OH | PCE |  |  | 2128.3 |  |  |  |
| NEIOH0829700 | 39.8172 | -84.0369 | US DOD WRIGHT-PATTERSON AFB OH | WPAFB, OH | PCE |  |  | 226.8 |  |  |  |
| NEIOH0857730 | 39.8156 | -84.1801 | WALL COLMONOY | DAYTON, OH | TCE |  |  |  | 4535.9 |  |  |
| NEIOH0857770 | 39.7959 | -84.134 | MULLINS RUBBER PRODUCTS INC. | RIVERSIDE, OH | TCE |  |  |  | 1814.4 |  |  |
| NEIOH17077 | 41.48774 | -81.73022 | CLEVELAND MANUFACTURING DIVISION | CLEVELAND, OH | PCE |  |  | 4329.3 |  |  |  |
| NEIOHRR255 | 39.8209 | -84.0068 | STADCO AUTOMATICS DIV. | FAIRBORN, OH | TCE |  |  |  | 2721.6 |  |  |
| NEIOHRR343 | 40.0396 | -84.1992 | HOBART CABINET | TROY, OH | PCE |  |  | 6350.3 |  |  |  |
| NEIOHRR364 | 39.9677 | -84.1986 | CAPTOR CORPORATION | TIPP CITY, OH | TCE |  |  |  | 2268.0 |  |  |
| NEIOHRR385 | 39.7818 | -84.1815 | B-N PLATING | DAYTON, OH | TCE |  |  |  | 3810.2 |  |  |
| NEIOHRR386 | 39.7696 | -84.1492 | STACO ENERGY PRODUCTS, INC. | DAYTON, OH | PCE |  |  | 1360.8 |  |  |  |
| NEIOHRR501 | 39.6276 | -84.2386 | HARTZELL MANUFACTURING CO. INC. | MIAMISBURG, OH | PCE |  |  | 3628.7 |  |  |  |
| NEIOHRR577 | 39.7909 | -84.1931 | ALPINE PRODUCTS MFG CO. INC. | DAYTON, OH | TCE |  |  |  | 4717.4 |  |  |
| NEIOHT$6567 | 39.763 | -84.1798 | WINSTON HEAT TREATING INC. | DAYTON, OH | PCE |  |  | 4082.3 |  |  |  |
| NEIOHT$6598 | 39.6534 | -84.2433 | DAYTON PROGRESS CORP. | WEST CARROLLTON, OH | TCE |  |  |  | 4989.5 |  |  |
| NEIOK1020 | 36.21221 | -95.87275 | AMERICAN AIRLINES INC | TULSA, OK | MC, PCE, TCE | 63.5 |  | 23586.8 | 4535.9 |  |  |
| NEIOK4211 | 36.15636 | -95.97131 | SOUTHWEST UNITED IND | TULSA, OK | PCE |  |  | 653.2 |  |  |  |
| NEIPA003347 | 40.57121 | -79.86357 | KINDER MORGAN INDIANOLA PLANT | INDIANOLA, PA | PCE |  |  | 26.3 |  |  |  |
| NEIPA1014907 | 39.91258 | -75.23281 | PECO ELECTRIC SHOP - OREGON | PHILADELPHIA, PA | PCE |  |  | 0.0 |  |  |  |
| NEIPA12304-3 | 41.8688 | -79.15029 | OSRAM SYLVANIA PROD /WARREN PLT | WARREN, PA | TCE |  |  |  | 6259.6 |  |  |
| NEIPA13304-3 | 39.96791 | -76.75471 | OSRAM SYLVANIA PROD /YORK BASE PROD PLT | YORK, PA | TCE |  |  |  | 7030.7 |  |  |
| NEIPA14-1682 | 40.25331 | -75.27985 | AMETEK INC/SELLERSVILLE | SELLERSVILLE, PA | TCE |  |  |  | 635.0 |  |  |
| NEIPA2187 | 41.1198 | -78.76116 | SENSUS METERING SYS/PLT 1 LIBERTY BLVD | DUBOIS, PA | PCE, TCE |  |  | 1460.6 | 1356.6 |  |  |
| NEIPA2244 | 40.02633 | -75.03164 | MODEL FINISHING CO | PHILADELPHIA, PA | TCE |  |  |  | 907.2 |  |  |
| NEIPA23-0419 | 40.1522 | -75.01327 | BOEKEL IND INC/FEASTERVILLE | FEASTERVILLE, PA | TCE |  |  |  | 3538.0 |  |  |
| NEIPA23-1498 | 40.41553 | -75.38813 | BRACALENTE MFG CO INC/TRUMBAUERSVILLE | TRUMBAURSVILLE, PA | TCE |  |  |  | 217.7 |  |  |
| NEIPA23-2230 | 41.98826 | -76.51552 | RYNONE MFG CORP/SAYRE PLT | SAYRE, PA | MC | 1542.2 |  |  |  |  |  |
| NEIPA23-2947 | 40.10723 | -79.58406 | SUMMERILL TUBE CORP/SCOTTDALE PLT | SCOTTDALE, PA | TCE |  |  |  | 24031.3 |  |  |
| NEIPA25-0932 | 41.76938 | -78.08346 | EMPORIUM SPECIALTIES/FOSTER AVE PLT | AUSTIN, PA | TCE |  |  |  | 743.9 |  |  |
| NEIPA25-1054 | 40.29743 | -79.39162 | LATRONICS CORP/LATROBE PLT | LATROBE, PA | TCE |  |  |  | 1306.3 |  |  |
| NEIPA25-1185 | 39.85428 | -79.74334 | GEROME MFG CO INC/OLIVER | UNIONTOWN, PA | TCE |  |  |  | 522.3 |  |  |
| NEIPA25-1355 | 41.79995 | -78.63341 | KEYSTONE THERMOMETRICS/MT JEWETT PLT | MOUNT JEWETT, PA | TCE |  |  |  | 58.5 |  |  |
| NEIPAT$1635 | 41.33338 | -80.45004 | DAMASCUS BISHOP TUBE/GREENVILLE | GREENVILLE, PA | TCE |  |  |  | 16789.3 |  |  |
| NEIPAT$1693 | 42.00418 | -80.23479 | SPECTRUM CONTROL INC/AVONIA ROAD | FAIRVIEW, PA | TCE |  |  |  | 271.2 |  |  |
| NEIPAT$2047 | 39.86984 | -75.32073 | BOEING ROTOCRAFT MANAGEMENT CENTER/RIDLEY | PHILADELPHIA, PA | MC, TCA, TCE | 2169.3 | 232.4 |  | 1088.6 |  |  |
| NEIRCA036401 | 37.50651 | -121.9545 | CHA INDUSTRIES | FREMONT, CA | TCA |  | 39.5 |  |  |  |  |
| NEIRCA038551 | 38.20633 | -122.1423 | YOUNG PRODUCTS | SUISUN CITY, CA | TCA |  | 410.1 |  |  |  |  |
| NEIRCA303707 | 37.39569 | -122.115 | BELL INDUSTRIES, PRECISION MET | MOUNTAIN VIEW, CA | TCE |  |  |  | 317.1 |  |  |
| NEIRCA310374 | 37.37876 | -121.9619 | SDL INC | SANTA CLARA, CA | Chloroform |  |  |  |  |  | 452.9 |
| NEIRCA310521 | 37.51313 | -122.2587 | COMMUNICATIONS & POWER INDUSTR | SAN CARLOS, CA | TCA, TCE |  | 1838.3 |  | 1133.7 |  |  |
| NEIRCA310581 | 37.77584 | -122.2403 | REGENCY RESTORATION & ANTIQUES | OAKLAND, CA | MC | 180.5 |  |  |  |  |  |
| NEIRCA310599 | 37.76687 | -122.219 | SANTANA'S FURNITURE REFINISH | OAKLAND, CA | MC | 827.2 |  |  |  |  |  |
| NEIRCA311021 | 37.37912 | -121.9719 | MICREL SYNERGY SEMICONDUCTOR | SANTA CLARA, CA | MC | 7.3 |  |  |  |  |  |
| NEIRCA311178 | 37.41 | -121.9276 | LOCKHEED MARTIN FAIRCHILD SYST | MILPITAS, CA | TCA |  | 7.6 |  |  |  |  |
| NEIRCA311226 | 38.0132 | -122.038 | STRIPPING WORKSHOP SERVICE GRO | CONCORD, CA | MC | 3308.8 |  |  |  |  |  |
| NEIRCA311329 | 37.41268 | -121.955 | SUPERTEX INC | SAN JOSE, CA | TCA |  | 9.0 |  |  |  |  |
| NEIRI01004 | 41.86247 | -71.34398 | HONEYWELL SENSING & CONTROL | PAWTUCKET, RI | MC | 104.8 |  |  |  |  |  |
| NEIRIAMDI643 | 41.05562 | -94.34343 | FANSTEEL WELLMAN DYNAMICS | CRESTON, IA | PCE |  |  | 5428.5 |  |  |  |
| NEIRMN300066 | 45.0635 | -93.2683 | KURT MANUFACTURING INC - MAIN ST | FRIDLEY, MN | TCE |  |  |  | 1013.6 |  |  |
| NEIRMN301074 | 44.9549 | -93.2267 | HIAWATHA METALCRAFT INC | MINNEAPOLIS, MN | TCE |  |  |  | 2320.1 |  |  |
| NEIRMN500041 | 44.8962 | -94.3801 | NEW DIMENSION PLATING | HUTCHINSON, MN | TCE |  |  |  | 1231.8 |  |  |
| NEIROR686964 | 45.50021 | -122.8227 | TEKTRONIX, INC. | BEAVERTON, OR | TCE |  |  |  | 196.9 |  |  |
| NEIRSC0-0021 | 34.20613 | -82.12668 | TYCO HEALTHCARE/KENDALL | GREENWOOD, SC | PCE |  |  | 0.5 |  |  |  |
| NEIRSC156063 | 33.94529 | -81.12106 | EAGLE AVIATION INC | WEST COLUMBIA, SC | MC | 36.3 |  |  |  |  |  |
| NEISC0040-00 | 34.16874 | -82.40025 | PIRELLI POWER CABLE:ABBEVILLE | ABBEVILLE, SC | TCA |  | 100.7 |  |  |  |  |
| NEISCT$3360 | 34.12582 | -80.87027 | FN MANUFACTURING | COLUMBIA, SC | TCE |  |  |  | 1946.8 |  |  |
| NEISCT$3554 | 34.69189 | -82.51245 | GRIFFIN THERMAL PRODUCTS | PIEDMONT, SC | TCE |  |  |  | 5407.3 |  |  |
| NEIT$FNP1184 | 45.57216 | -122.6005 | PORTLAND WILLAMETTE | PORTLAND, OR | TCE |  |  |  | 3628.7 |  |  |
| NEITN0470 | 35.0196 | -85.29715 | CHATTANOOGA ARMATURE WORKS, INC. | CHATTANOOGA, TN | TCE |  |  |  | 376.5 |  |  |
| NEITNT$5022 | 35.9569 | -83.8267 | AMERICAN SAFETY RAZOR, INC. | KNOXVILLE, TN | TCE |  |  |  | 15694.3 |  |  |
| NEITX48037F0 | 33.472 | -94.39 | SAME | TEXARKANA, TX | TCA |  | 74.4 |  |  |  |  |
| NEITXRDF0558 | 33.00444 | -97.31056 | AIRCRAFT ENGINE OVERHAUL | FORT WORTH, TX | TCE |  |  |  | 3420.1 |  |  |
| NEITXT$11144 | 32.54306 | -97.03944 | TUBE FORMING INC | CARROLLTON, TX | TCE |  |  |  | 22035.5 |  |  |
| NEITXT$11265 | 32.92778 | -96.75778 | SEMICONDUCTOR MFG | DALLAS, TX | PCE |  |  | 3240.6 |  |  |  |
| NEITXT$11375 | 32.93417 | -97.09861 | STANDARD MOTOR PRODUCTS | GRAPEVINE, TX | TCE |  |  |  | 2909.0 |  |  |
| NEITXT$11600 | 30.39222 | -95.47361 | ROBBINS & MYERS ENERGY | WILLIS, TX | TCE |  |  |  | 4980.4 |  |  |
| NEITXT$11693 | 29.78898 | -95.12699 | CHANNELVIEW COMPLEX | CHANNELVIEW, TX | TCA |  | 762.0 |  |  |  |  |
| NEIUT0351664 | 40.84972 | -111.9667 | DELTA AIRLINES AT SLC INT'L AIRPORT | SALT LAKE CITY, UT | TCE |  |  |  | 419.9 |  |  |
| NEIUT10555 | 40.69778 | -111.9008 | RUBBER ENGINEERING | SALT LAKE CITY, UT | PCE |  |  | 121.1 |  |  |  |
| NEIVA0470044 | 38.46973 | -78.00837 | THE ROCHESTER CORPORATION | CULPEPER, VA | PCE, TCE |  |  | 0.1 | 665.8 |  |  |
| NEIVAT$2444 | 37.49793 | -77.5928 | SUPER RADIATOR COILS | CHESTERFIELD, VA | PCE |  |  | 27034.1 |  |  |  |
| NEIWA0072 | 47.67515 | -117.1998 | HONEYWELL ELECTRONIC MATERIALS | SPOKANE, WA | MC | 544.3 |  |  |  |  |  |
| NEIWA13120 | 47.91961 | -122.2772 | BOEING COMMERCIAL AIRPLANE GROUP - EVERETT | EVERETT, WA | TCE |  |  |  | 27035.9 |  |  |
| NEIWA14082 | 47.56341 | -122.6327 | U S NAVY PUGET SOUND NAVAL SHIPYARD, PSNS | BREMERTON, WA | MC, TCA, TCE | 1856.6 | 0.5 |  | 990.6 |  |  |
| NEIWI1314880 | 43.3978 | -88.1999 | BARTON PRODUCTS CORPORTATION | WEST BEND, WI | TCE |  |  |  | 700.8 |  |  |
| NEIWI1541294 | 42.7735 | -89.29911 | SOUTHERN WISCONSIN METAL FABRICATION, INC. | EVANSVILLE, WI | TCE |  |  |  | 598.7 |  |  |
| NEIWI2410173 | 43.14874 | -88.01308 | PERLICK CORPORATION | MILWAUKEE, WI | TCE |  |  |  | 1261.4 |  |  |
| NEIWI2410368 | 43.04892 | -87.91577 | MILWAUKEE PLATING CO | MILWAUKEE, WI | TCE |  |  |  | 310.3 |  |  |
| NEIWI2419617 | 42.86723 | -87.98152 | GENERAL AUTOMOTIVE MANUFACTURING, LLC-W. AIRWAY | FRANKLIN, WI | TCE |  |  |  | 1609.8 |  |  |
| NEIWI2460526 | 43.37568 | -87.88265 | MOLDED DIMENSIONS | PORT WASHINGTON, WI | TCE |  |  |  | 4913.9 |  |  |
| NEIWI2520097 | 42.74784 | -87.80109 | E C STYBERG ENGINEERING CO INC | RACINE, WI | TCE |  |  |  | 1442.4 |  |  |
| NEIWI2650061 | 42.79042 | -88.38939 | CRUCIBLE MATERIALS CORP TRENT TUBE PLT 2 & 3 | EAST TROY, WI | TCE |  |  |  | 73081.4 |  |  |
| NEIWI2680147 | 43.08588 | -88.26501 | DYNEX-RIVETT, INC | PEWAUKEE, WI | TCE |  |  |  | 4226.1 |  |  |
| NEIWI2682381 | 43.04774 | -88.18331 | CASTING IMPREGNATORS OF WISCONSIN, INC. | WAUKESHA, WI | TCE |  |  |  | 3116.2 |  |  |
| NEIWI6030598 | 45.5438 | -92.01742 | AMERICAN TOOL COMPANY (FORMERLY IRWIN) | CUMBERLAND, WI | TCE |  |  |  | 6041.6 |  |  |
| NEIWI7440095 | 45.63191 | -89.39411 | PRECISION TWIST DRILL CO - RHINELANDER | RHINELANDER, WI | TCE |  |  |  | 1583.9 |  |  |
| NEIWIT$8642 | 44.95554 | -91.37273 | INDIANHEAD PLATING, INC. | CHIPPEWA FALLS, WI | TCE |  |  |  | 10142.3 |  |  |
| NEIWV0110009 | 38.42445 | -82.43195 | SWVA, INC. | HUNTINGTON, WV | TCA, PCE |  | 2.5 | 2.4 |  |  |  |

1 MC = Methylene Chloride;  TCA = trichloroethane (is not a carcinogen so does not contribute to facility-total MC-equivalent emissions in Exhibit E-2); PCE = Tetrachloroethylene (perchloroethylene); TCE = trichloroethylene; C Tetrachloride = Carbon Tetrachloride.  Chloroform is not a carcinogen so does not contribute to facility-total MC-equivalent emissions in Exhibit B-2.

Appendix C

Stack Parameters Used for HEM-SCREEN Modeling of 1999 and 2002 Halogenated Solvent Cleaning Facilities

Exhibit C-1

Stack Parameters Used in HEM-SCREEN for Halogenated Solvent Cleaning Facilities

| Stack Height (meters) | Area (square meters) | Vent Type | Stack Diameter (meters) | Gas Exit Velocity (m/s) | Gas Exit Temperature (K) |
| --- | --- | --- | --- | --- | --- |
| 9.42 | 400 | Vertical | 0.53 | 9.08 | 305 |

Appendix D

Aerospace, Military Depot, Narrow Tube, and Continuous Web Cleaning Sector Subsets of 1999 and 2002 Halogenated Solvent Cleaning Facilities

Exhibit D-1

Halogenated Solvent Cleaning Facilities in the Aerospace Sector1

| 1999 | 2002 |
| --- | --- |
| ID | Name | ID | Name |
| 39-1 | AMERICAN AIRLINES | NEI2162 | MCDONNELL DOUGLAS ASTRONAUTICS CO |
| 40-4 | BOEING COMPANY | NEI5994 | LOCKHEED MARTIN CORP/MICHOUD |
| NTI814 | ATLANTIC RESEARCH | NEI6536 | VOUGHT JEFFERSON ST FACIL |
| NTI1608 | STANLEY AVIATION CORP | NEI8320 | GOODRICH CORPORATION |
| NTI2162 | MCDONNELL DOUGLAS ASTRONAUTICS CO | NEI10885 | GULFSTREAM AEROSPACE CORP. |
| NTI7203 | TEXTRON LYCOMING/OLIVER STREET PLT | NEI11188 | MARSHALL STREET FACILITY |
| NTI12320 | NORTHWEST AIRLINES INC/MPLS/ST PAUL AIRP | NEI12930 | TINKER AFB US AIR FORCE LOGISTICS CTR |
| NTI12371 | DALLAS FORTWORTH INTRNTNL AIRPORT | NEI12974 | HONEYWELL INC |
| NTI12595 | BELL HELICOPTER TEXTRON INC | NEI20231 | ACE CLEARWATER ENTER. |
| NTI12925 | GULFSTREAM AEROSPACE TECHNOLOGIES | NEI20237 | ADAMS RITE SABRE INTERNATIONAL |
| NTI12973 | THE NORDAM GROUP | NEI20243 | AERO ENGINES INC |
| NTI12974 | ALLIED SIGNAL - LORI, INC. | NEI20247 | AEROSPACE ALUMINUM HEAT TREATI |
| NTI13294 | ALLIEDSIGNAL AEROSPACE SYSTEMS | NEI20257 | AIRCRAFT X-RAY LABS INC |
| NTI13336 | BOEING COMPANY (THE) | NEI20273 | AMERICAN AIRLINES INC (EIS USE |
| NTI18485 | GARRETT ENGINE DIVISION | NEI20348 | BW/IP INTERNATIONAL INC |
| NTI19632 | DEXTER HYSOL AEROSPACE, INC | NEI20370 | BLAIR'S METAL POLISHING |
| NTI20231 | ACE CLEARWATER ENTER. | NEI20497 | COMPOSITE STRUCTURES LLC |
| NTI20237 | ADAMS RITE SABRE INTERNATIONAL | NEI20543 | CV INTL INC |
| NTI20243 | AERO ENGINES INC | NEI20572 | DELTA AIR LINES, INC |
| NTI20245 | AEROJET GENCORP, AEROJET ELECT | NEI20618 | EEMCO, DATRON INC DIV |
| NTI20247 | AEROSPACE ALUMINUM HEAT TREATI | NEI20749 | HAGELIN AIRCRAFT MOTORS CO INC |
| NTI20256 | AIRCRAFT CYLINDER & TURBINE IN | NEI20756 | HAWKER PACIFIC INC |
| NTI20257 | AIRCRAFT X-RAY LABS INC | NEI20787 | HUGHES AIRCRAFT CO, EDSG |
| NTI20273 | AMERICAN AIRLINES INC (EIS USE | NEI21002 | MCDONNELL DOUGLAS AEROSPACE |
| NTI20348 | BW/IP INTERNATIONAL INC | NEI21011 | MENASCO MFG CO (EIS USE) |
| NTI20511 | CONTINENTAL AIRLINES INC (NSR | NEI21045 | MONOGRAM AEROSPACE FASTENERS, |
| NTI20522 | COURTAULDS AEROSPACE INC | NEI21097 | ONTIC ENGINEERING & MANUFACTUR |
| NTI20527 | CRANE CO, HYDRO-AIRE DIV | NEI21110 | PACIFIC AIRMOTIVE CORP |
| NTI20543 | CV INTL INC | NEI21203 | R & B AIRCRAFT SUPPLY INC |
| NTI20572 | DELTA AIR LINES, INC | NEI21282 | SENIOR FLEXONICS INC/STAINLESS STEEL DVN |
| NTI20618 | EEMCO, DATRON INC DIV | NEI21439 | TRANS WORLD AIRLINES INC |
| NTI20749 | HAGELIN AIRCRAFT MOTORS CO INC | NEI22099 | HUGHES AIRCRAFT CO, MICROELECT |
| NTI20787 | HUGHES AIRCRAFT CO, EDSG | NEI22119 | KAISER ELECTROPRECISION |
| NTI21002 | MCDONNELL DOUGLAS AEROSPACE | NEI22153 | MCDONNELL DOUGLAS CORP, SUB OF BOEING CO |
| NTI21011 | MENASCO MFG CO (EIS USE) | NEI22192 | PARKER HANNIFIN AEROSPACE CORP |
| NTI21045 | MONOGRAM AEROSPACE FASTENERS, | NEI22280 | TELONIC BERKELEY INC |
| NTI21085 | NORTHROP GRUMMAN CORP | NEI22326 | VESPER CORP |
| NTI21097 | ONTIC ENGINEERING & MANUFACTUR | NEI22332 | WEBER AIRCRAFT INC |
| NTI21110 | PACIFIC AIRMOTIVE CORP | NEI22458 | ROHR,INC |
| NTI21203 | R & B AIRCRAFT SUPPLY INC | NEI22485 | AEROJET FINE CHEMICAL |
| NTI21282 | SENIOR FLEXONICS INC/STAINLESS | NEI22848 | NAVAL AIR WEAPONS STATION |
| NTI21439 | TRANS WORLD AIRLINES INC | NEI23510 | UNITED AIRLINES, MAINTENANCE O |
| NTI21478 | UNITED AERONAUTICAL CORP | NEI25016 | PACIFIC AEROSPACE SERVICES |
| NTI21520 | VICKERS INC, STERER DIVISION | NEI25264 | UNITED TECHNOLOGIES CORPORATIO |
| NTI22099 | HUGHES AIRCRAFT CO, MICROELECT | NEI25481 | OEA AREOSPACE INC |
| NTI22119 | KAISER ELECTROPRECISION | NEI26056 | PTI TECHNOLOGIES INC. |
| NTI22192 | PARKER HANNIFIN AEROSPACE CORP | NEI26060 | SANTA SUSANA FIELD LABORATORY |
| NTI22280 | TELONIC BERKELEY INC | NEI26095 | TELAIR INTERNATIONAL |
| NTI22326 | VESPER CORP | NEI32072 | ROLLS-ROYCE CORPORATION. PLANT 5 & 8 |
| NTI22332 | WEBER AIRCRAFT INC | NEI32831 | BOEING COMMERCIAL AIRPLANE GROUP |
| NTI22458 | ROHR,INC | NEI34485 | SABRELINER CORPORATION-PERRYVILLE PLANT |
| NTI22485 | AEROJET | NEI34514 | AMERICAN AIRLINES-MCI MAINTENANCE AND ENGINEERING |
| NTI23510 | UNITED AIRLINES, MAINTENANCE O | NEI34632 | MCDONNELL DOUGLAS CORP./BOEING COMPANY-LINDBERGH P |
| NTI24183 | METAL FUSION INC | NEI34682 | AMERICAN AIRLINES INC-OLD NATURAL BRIDGE RD |
| NTI24404 | LUCAS AVIATION - SANTA MARIA | NEI42005 | PROMONTORY PLANT |
| NTI25016 | PACIFIC AEROSPACE SERVICES | NEI43378 | VOUGHT AIRCRAFT INDUSTRIES, INC |
| NTI25264 | UNITED TECHNOLOGIES CORPORATIO | NEI45203 | MARINE CORPS AIR STATION |
| NTI26056 | PTI TECHNOLOGIES INC. | NEI45208 | NAVAL AIR DEPOT |
| NTI26060 | ROCKETDYNE DIVISION | NEI53352 | DANVILLE METAL STAMPING CO |
| NTI26095 | THE TALLEY CORPORATION | NEI2CA272317 | SPECIALIZED PROCESSING CO., IN |
| NTI32072 | ALLISON ENGINE COMPANY, INC. PLANT 5 & 8 | NEI2CA512150 | NASA DRYDEN FLIGHT RESEARCH CR |
| NTI32831 | BOEING COMMERCIAL AIRPLANE GROUP | NEI2CO1238 | VECTOR CORPORATION |
| NTI32838 | RAYTHEON AIRCRAFT COMPANY | NEI2MIN6857 | PPI AEROSPACE ACQUISITION, LLC |
| NTI34472 | SABRELINER CORPORATION | NEI2MIN6858 | PPI AEROSPACE ACQUISITION, LLC |
| NTI34514 | TRANS WORLD AIRLINES INC | NEI2MO1489 | GKN AEROSPACE SERVICES INC-BERKELEY |
| NTI34540 | MCDONNELL DOUGLAS CORPORATION | NEI2UT11674 | SKYWEST AIRLINES AT SLC INT'L AIRPORT |
| NTI34632 | MCDONNELL DOUGLAS CORPORATION | NEICA00160 | ROLLS-ROYCE ENGINE SERVICES - |
| NTI34682 | TRANS WORLD AIRLINES | NEICA0371361 | ALLIED-SIGNAL INC,GARRETT GEN |
| NTI41653 | GE ENGINESERVICES--DALLAS LP | NEICA0371372 | ALLIEDSIGNAL AEROSPACE, W COAS |
| NTI42005 | PROMONTORY PLANT | NEICA0371508 | THE BOEING COMPANY |
| NTI42445 | ALLEGANY BALLISTICS LABORATORY | NEICA0371587 | THE BOEING COMPANY |
| NTI43378 | AEROSTRUCTURES CORPORATION, THE | NEICA0379995 | HR TEXTRON INC. |
| NTI53352 | DANVILLE METAL STAMPING CO. | NEICA0379999 | HR TEXTRON INC |
| NTI54284 | BOEING COMMERCIAL AIRPLANE (RENTON) | NEICA06029F0 | EDWARDS AIR FORCE BASE |
| NTICA00160 | ROLLS-ROYCE ENGINE SERVICES - | NEICA0732681 | ROHR INDUSTRIES. |
| NTICA0371263 | NORTHROP GRUMMAN CORP, MASD | NEICA0733201 | USMC AIR STATION / MIRAMAR |
| NTICA0371361 | ALLIED-SIGNAL INC,GARRETT GEN | NEICA0854523 | LOCKHEED MARTIN CORPORATION |
| NTICA0371372 | ALLIEDSIGNAL AEROSPACE, W COAS | NEICA0854766 | LOCKHEED MARTIN CORPORATION, M |
| NTICA0371508 | THE BOEING COMPANY | NEIFL1010335 | PALL AEROPOWER CORP |
| NTICA0371561 | THE BOEING COMPANY | NEIFLR023003 | TIMCO |
| NTICA0371587 | THE BOEING COMPANY | NEIIL0458147 | MECO INC |
| NTICA0379 | HONEYWELL INTERNATIONAL INC | NEIIL1839900 | DANVILLE METAL STAMPING CO |
| NTICA0379995 | HR TEXTRON INC. | NEIIL227 | WOODWARD GOVERNOR CO |
| NTICA0379999 | HR TEXTRON INC | NEIKS00075 | CESSNA AIRCRAFT CO.-PAWNEE FACILITY |
| NTICA0592031 | TEXTRON AEROSPACE FASTENERS | NEIKS00165 | GLOBE ENGINEERING COMPANY, INC. |
| NTICA0732551 | COMPOSITE OPTICS, INC. | NEIKST$10304 | LEARJET, INC. |
| NTICA0732681 | ROHR INDUSTRIES. | NEIKST$10326 | CESSNA AIRCRAFT DIVISION - MID-CONTINENT |
| NTICA0773905 | BP CHEMICALS INC | NEIMI065A163 | PRATT & WHITNEY AUTOAIR |
| NTICA0854523 | LOCKHEED MARTIN CORPORATION | NEIMIN3303 | DUNCAN AVIATION INC. |
| NTICA0854761 | LOCKHEED MARTIN CORPORATION, M | NEINC0216 | US AIRWAYS, FOUR (4) SITE LOCATIONS |
| NTICA0854766 | LOCKHEED MARTIN CORPORATION, M | NEIOK1020 | AMERICAN AIRLINES INC |
| NTICA1905024 | NORTHROP GRUMMAN, SITE 4 | NEIPAT$2047 | BOEING ROTOCRAFT MANAGEMENT CENTER/RIDLEY |
| NTICAT$12604 | NORTHROP GRUMMAN CORP, AIRCRAF | NEIRCA311178 | LOCKHEED MARTIN FAIRCHILD SYST |
| NTICO1819 | LEARJET, INC. - DIA | NEIRSC156063 | EAGLE AVIATION INC |
| NTIFL0250827 | B F GOODRICH | NEITXRDF0558 | AIRCRAFT ENGINE OVERHAUL |
| NTIFL0610023 | THE NEW PIPER AIRCRAFT, INC | NEIUT0351664 | DELTA AIRLINES AT SLC INT'L AIRPORT |
| NTIFL1010335 | PALL AEROPOWER CORP | NEIWA13120 | BOEING COMMERCIAL AIRPLANE GROUP - EVERETT |
| NTIFLR023003 | TIMCO |  |  |
| NTIIL0458147 | MECO INC |  |  |
| NTIIL1839900 | DANVILLE METAL STAMPING CO. INC. |  |  |
| NTIIL201109 | HAMILTON SUNDSTRAND |  |  |
| NTIIL227 | WOODWARD GOVERNOR CO. |  |  |
| NTIIL292 | HAMILTON SUNDSTRAND |  |  |
| NTIKS00075 | CESSNA AIRCRAFT CO.-PAWNEE FACILITY |  |  |
| NTIKS00165 | GLOBE ENGINEERING |  |  |
| NTIOHT$6556 | MCCAULEY PROPELLER SYS. |  |  |
| NTIOK1229 | CIMARRON AIRCRAFT CORP. |  |  |
| NTIOK4206 | LIMCO AIREPAIR |  |  |
| NTITXRDF0558 | TEXAS AEROENGINE SERVICE LLC |  |  |
| NTIWA13117 | BOEING COMMERCIAL AIRPLANE (AUBURN) |  |  |
| NTIWA13120 | BOEING COMMERCIAL AIRPLANE GROUP - EVERETT |  |  |
| NTIWA15119 | GOODRICH AVIATION |  |  |
| NTIWA17771 | BOEING COMMERCIAL AIRPLANE (FREDERICKSON) |  |  |
| NTIWA28573 | EXOTIC METALS FORMING CO |  |  |

1 Facilities not emitting known carcinogens are in italics.

Exhibit D-2

Halogenated Solvent Cleaning Facilities in the Military Depot Sector1

| 1999 | 2002 |
| --- | --- |
| ID | Name | ID | Name |
| NTI18329 | ANNISTON ARMY DEPOT | NEI12422 | CORPUS CHRISTI ARMY DEPOT |
| NTI22632 | SACRAMENTO ARMY DEPOT | NEI18329 | ANNISTON ARMY DEPOT |
|  |  | NEI23615 | DEFENSE DISTRIB DEPOT SAN JOAQ |

1 Facilities not emitting known carcinogens are in italics.

Exhibit D-3

Halogenated Solvent Cleaning Facilities in the Narrow Tube Sector1

| 1999 | 2002 |
| --- | --- |
| ID | Name | ID | Name |
| NTI5410 | TUBE METHODS INC/BRIDGEPORT | NEI5410 | TUBE METHODS INC/BRIDGEPORT |
| NTI7345 | HANDY & HARMAN TUBE /EAST NORRITON | NEI7069 | SALEM TUBE INC/SALEM TUBE INC |
| NTI7347 | UNIFORM TUBES INC/COLLEGEVILLE | NEI7345 | HANDY & HARMAN TUBE /EAST NORRITON |
| NTI7348 | SUPERIOR TUBE CO/LOWER PROVIDENCE | NEI7347 | UNIFORM TUBES INC/COLLEGEVILLE |
| NTI13146 | OAKLEY INDUSTRIES INC OAKLEY TUBE DIV | NEI7348 | SUPERIOR TUBE CO/LOWER PROVIDENCE |
| NTI21181 | PRECISION TUBE BENDING | NEI7352 | PRECISION TUBE COMPANY |
| NTI46675 | WESTERN PNEUMATIC TUBE COMPANY | NEI11519 | LINDERME TUBE COMPANY (THE) |
| NTITXT$11144 | TUBE FORMING INC | NEI13146 | OAKLEY INDUSTRIES INC OAKLEY TUBE DIV |
| NTIWA18093 | TUBETRONICS (KENT DIVISION) | NEI33721 | PLYMOUTH TUBE COMPANY |
| NTIWI2650061 | CRUCIBLE MATERIALS CORP TRENT TUBE PLT 2 & 3 | NEI2RIAIR19 | A.T. WALL CO. |
|  |  | NEIART$10939 | AMERICAN TUBING,INCORPORATED |
|  |  | NEIPA23-2947 | SUMMERILL TUBE CORP/SCOTTDALE PLT |
|  |  | NEIPAT$1635 | DAMASCUS BISHOP TUBE/GREENVILLE |
|  |  | NEIWI2650061 | CRUCIBLE MATERIALS CORP TRENT TUBE PLT 2 & 3 |

1 Facilities not emitting known carcinogens are in italics.

Exhibit D-4

Halogenated Solvent Cleaning Facilities in the Continuous Web Cleaning Sector1

| 1999 | 2002 |
| --- | --- |
| ID | Name | ID | Name |
| NTI2733 | JOHNSON & JOHNSTON ASSOCIATES | NEI2733 | JOHNSON & JOHNSTON ASSOC. INC. |
| NTI6360 | OLIN CORP. SOMERS THIN STRIP BRASS GROUP | NEI6360 | SOMERS THIN STRIP |
| NTI7218 | ARCOS DIV HOSKINS MF/MT CARMEL PLT | NEI7218 | ARCOS IND LLC/MT CARMEL PLT |
| NTI10900 | LTV-COPPERWELD FAYETTEVILLE DIV. | NEI12240 | ALCOA INC. |
| NTI12240 | ALCOA INC. | NEI20508 | CONSOLIDATED FILM INDUSTRIES |
| NTI20508 | CONSOLIDATED FILM INDUSTRIES | NEI20575 | DELUXE LABORATORIES INC,DELUXE |
| NTI20575 | DELUXE LABORATORIES INC,DELUXE | NEI21378 | TECHNICOLOR INC |
| NTI21378 | TECHNICOLOR INC | NEITNT$5022 | AMERICAN SAFETY RAZOR, INC. |
| NTITNT$5022 | AMERICAN SAFETY RAZOR KNOXVILLE DIV. |  |  |
| NTIVAT$2612 | AMERICAN SAFETY RAZOR INC. |  |  |

1 Facilities not emitting known carcinogens are in italics.

Appendix E

HEM-SCREEN Input Files for Halogenated Solvent Cleaning Facilities

Exhibit E-1

Selected Fields from the 1999 HEM-SCREEN Input for Carcinogen-Emitting Halogenated Solvent Cleaning Facilities1

| Unit Risk Factor (ug/m3)-1 | Facility Name | Latitude2 | Longitude2 | OPPTS3 MC4-Equivalent Emission Rate (kg/yr) | CalEPA3 MC4-Equivalent Emission Rate (kg/yr) |
| --- | --- | --- | --- | --- | --- |
| 4.7E-07 | 2-1 | 425547 | 763427 | 2.18E+03 | 2.18E+03 |
| 4.7E-07 | 3-1 | 430635 | 760916 | 1.43E+04 | 1.43E+04 |
| 4.7E-07 | 4-1 | 430657 | 772921 | 7.43E+03 | 7.43E+03 |
| 4.7E-07 | 6-1 | 404320 | 735655 | 1.34E+04 | 1.34E+04 |
| 4.7E-07 | 8-1 | 405140 | 730926 | 4.14E+02 | 4.14E+02 |
| 4.7E-07 | 14-1 | 404543 | 722704 | 4.32E+03 | 4.32E+03 |
| 4.7E-07 | 16-1 | 430536 | 751535 | 2.39E+03 | 2.39E+03 |
| 4.7E-07 | 19-1 | 420252 | 790754 | 1.15E+04 | 1.15E+04 |
| 4.7E-07 | 22-1 | 411242 | 735912 | 2.72E+04 | 2.72E+04 |
| 4.7E-07 | 31-2 | 352542 | 972422 | 1.21E+04 | 1.00E+05 |
| 4.7E-07 | 31-3 | 292224 | 983257 | 1.08E+04 | 8.99E+04 |
| 4.7E-07 | 31-5 | 473349 | 1223737 | 2.84E+03 | 2.84E+03 |
| 4.7E-07 | 36-1 | 341310 | 920022 | 8.06E+04 | 6.70E+05 |
| 4.7E-07 | 37-1 | 352820 | 932826 | 2.76E+05 | 2.76E+05 |
| 4.7E-07 | 38-1 | 350324 | 1063314 | 7.09E+02 | 1.01E+03 |
| 4.7E-07 | 39-1 | 361232 | 955206 | 9.39E+04 | 4.19E+05 |
| 4.7E-07 | 40-4 | 471841 | 1222148 | 2.69E+04 | 4.90E+04 |
| 4.7E-07 | 42-1 | 361037 | 955103 | 1.71E+04 | 1.71E+04 |
| 4.7E-07 | 44-1 | 324917 | 965034 | 6.50E+03 | 6.50E+03 |
| 4.7E-07 | 45-1 | 325653 | 965005 | 1.26E+03 | 1.26E+03 |
| 4.7E-07 | 49-1 | 331113 | 961748 | 3.91E+03 | 3.91E+03 |
| 4.7E-07 | 53-1 | 324449 | 965355 | 1.58E+03 | 1.31E+04 |
| 4.7E-07 | 54-1 | 295409 | 975701 | 1.03E+05 | 1.03E+05 |
| 4.7E-07 | 56-1 | 324516 | 985403 | 3.16E+03 | 3.16E+03 |
| 4.7E-07 | 57-2 | 330014 | 971837 | 8.91E+03 | 8.91E+03 |
| 4.7E-07 | 59-1 | 322848 | 994250 | 1.27E+04 | 1.27E+04 |
| 4.7E-07 | 60-1 | 322428 | 994329 | 3.04E+04 | 3.04E+04 |
| 4.7E-07 | 61-1 | 325713 | 965310 | 6.39E+04 | 6.39E+04 |
| 4.7E-07 | 75-1 | 407969 | 864630 | 2.87E+02 | 2.87E+02 |
| 4.7E-07 | 78-1 | 414139 | 855318 | 1.49E+03 | 1.49E+03 |
| 4.7E-07 | 80-1 | 391059 | 855341 | 1.90E+03 | 1.90E+03 |
| 4.7E-07 | 81-1 | 394602 | 860642 | 3.17E+04 | 3.17E+04 |
| 4.7E-07 | 82-1 | 394547 | 860820 | 4.57E+02 | 3.80E+03 |
| 4.7E-07 | 83-1 | 411631 | 855122 | 4.90E+03 | 4.90E+03 |
| 4.7E-07 | 84-1 | 375813 | 873233 | 3.37E+03 | 3.37E+03 |
| 4.7E-07 | 85-1 | 402720 | 860613 | 3.32E+02 | 3.32E+02 |
| 4.7E-07 | 86-2 | 404556 | 860333 | 1.56E+04 | 1.56E+04 |
| 4.7E-07 | 87-1 | 412102 | 850849 | 8.24E+02 | 8.24E+02 |
| 4.7E-07 | 88-1 | 412102 | 850836 | 3.55E+01 | 3.55E+01 |
| 4.7E-07 | 90-1 | 403553 | 845727 | 4.27E+03 | 4.27E+03 |
| 4.7E-07 | 91-1 | 395516 | 861536 | 7.33E+01 | 7.33E+01 |
| 4.7E-07 | 92-1 | 401556 | 854904 | 1.31E+04 | 1.31E+04 |
| 4.7E-07 | 93-1 | 414050 | 855512 | 2.35E+03 | 2.35E+03 |
| 4.7E-07 | 94-1 | 393307 | 862212 | 3.72E+03 | 3.72E+03 |
| 4.7E-07 | 95-1 | 393853 | 850819 | 8.71E+04 | 8.71E+04 |
| 4.7E-07 | 97-1 | 404929 | 845629 | 4.82E+04 | 4.82E+04 |
| 4.7E-07 | 98-1 | 411410 | 855214 | 2.44E+03 | 2.44E+03 |
| 4.7E-07 | 99-1 | 382048 | 873422 | 6.33E+02 | 6.33E+02 |
| 4.7E-07 | 100-1 | 382142 | 854850 | 1.78E+04 | 1.78E+04 |
| 4.7E-07 | 101-1 | 412113 | 862002 | 2.32E+02 | 2.32E+02 |
| 4.7E-07 | 102-1 | 394602 | 860760 | 2.38E+04 | 2.38E+04 |
| 4.7E-07 | 104-1 | 398483 | 855456 | 5.20E+02 | 5.20E+02 |
| 4.7E-07 | 105-1 | 390733 | 855751 | 3.27E+04 | 3.27E+04 |
| 4.7E-07 | 106-1 | 382210 | 865634 | 2.13E+03 | 2.13E+03 |
| 4.7E-07 | 107-1 | 381732 | 854755 | 1.58E+03 | 1.58E+03 |
| 4.7E-07 | 108-1 | 393118 | 854721 | 2.86E+03 | 2.38E+04 |
| 4.7E-07 | 109-1 | 394513 | 860612 | 1.47E+04 | 1.47E+04 |
| 4.7E-07 | 111-1 | 395234 | 860460 | 7.76E+04 | 7.76E+04 |
| 4.7E-07 | 112-1 | 410510 | 851411 | 2.89E+05 | 2.89E+05 |
| 4.7E-07 | 113-1 | 413830 | 852331 | 1.27E+04 | 1.27E+04 |
| 4.7E-07 | 114-1 | 414122 | 855643 | 2.04E+04 | 2.04E+04 |
| 4.7E-07 | 115-1 | 382036 | 873346 | 2.25E+04 | 1.87E+05 |
| 4.7E-07 | 116-1 | 405245 | 851041 | 1.39E+03 | 1.39E+03 |
| 4.7E-07 | 117-1 | 394225 | 862324 | 1.88E+04 | 1.88E+04 |
| 4.7E-07 | 118-1 | 414056 | 855532 | 9.90E+01 | 9.90E+01 |
| 4.7E-07 | 121-1 | 400016 | 865307 | 2.45E+05 | 2.45E+05 |
| 4.7E-07 | 122-1 | 382032 | 854957 | 1.01E+04 | 1.01E+04 |
| 4.7E-07 | 123-1 | 413925 | 861002 | 9.60E+03 | 9.60E+03 |
| 4.7E-07 | 124-1 | 413947 | 861353 | 2.27E+04 | 2.27E+04 |
| 4.7E-07 | 125-1 | 414108 | 855604 | 2.33E+05 | 2.33E+05 |
| 4.7E-07 | 129-1 | 432333 | 1231741 | 4.92E+02 | 4.09E+03 |
| 4.7E-07 | 130-1 | 473944 | 1222225 | 5.56E+03 | 5.56E+03 |
| 4.7E-07 | 130-2 | 473945 | 1222220 | 7.81E+03 | 7.81E+03 |
| 4.7E-07 | 133-1 | 452916 | 1223818 | 3.92E+03 | 3.92E+03 |
| 4.7E-07 | 144-1 | 452958 | 1224837 | 9.40E+02 | 9.40E+02 |
| 4.7E-07 | 145-1 | 452954 | 1224852 | 2.74E+03 | 2.74E+03 |
| 4.7E-07 | 147-1 | 473312 | 1221947 | 1.08E+04 | 1.08E+04 |
| 4.7E-07 | 150-1 | 472441 | 1221513 | 1.76E+04 | 1.76E+04 |
| 4.7E-07 | 151-1 | 472151 | 1221344 | 2.06E+03 | 1.71E+04 |
| 4.7E-07 | 152-1 | 474111 | 1171213 | 4.50E+01 | 4.50E+01 |
| 4.7E-07 | 153-1 | 473101 | 1202825 | 3.01E+03 | 2.51E+04 |
| 4.7E-07 | 154-1 | 473955 | 1222221 | 7.01E+03 | 7.01E+03 |
| 4.7E-07 | 164-1 | 413220 | 902730 | 7.68E+04 | 6.38E+05 |
| 4.7E-07 | 165-1 | 381131 | 785917 | 2.16E+05 | 2.16E+05 |
| 4.7E-07 | 165-2 | 355735 | 834937 | 1.00E+05 | 1.00E+05 |
| 4.7E-07 | 166-1 | 404810 | 762650 | 5.57E+03 | 4.62E+04 |
| 4.7E-07 | 167-1 | 425129 | 711105 | 6.61E+04 | 6.61E+04 |
| 4.7E-07 | 169-1 | 413206 | 730155 | 5.25E+04 | 5.25E+04 |
| 4.7E-07 | 170-1 | 405518 | 735139 | 3.31E+03 | 3.31E+03 |
| 4.7E-07 | NTI59 | 403103 | 794841 | 1.63E+02 | 1.63E+02 |
| 4.7E-07 | NTI180 | 384246 | 771413 | 2.37E+04 | 2.37E+04 |
| 4.7E-07 | NTI922 | 354823 | 901432 | 4.25E+05 | 4.25E+05 |
| 4.7E-07 | NTI946 | 393849 | 1045956 | 1.70E+04 | 1.70E+04 |
| 4.7E-07 | NTI965 | 400342 | 1051221 | 2.25E+02 | 2.25E+02 |
| 4.7E-07 | NTI968 | 400836 | 1050641 | 9.76E+01 | 9.76E+01 |
| 4.7E-07 | NTI1162 | 371911 | 804338 | 2.54E+03 | 2.54E+03 |
| 4.7E-07 | NTI1608 | 394509 | 1045235 | 5.67E+03 | 5.67E+03 |
| 4.7E-07 | NTI1830 | 384831 | 1044329 | 2.28E+03 | 1.89E+04 |
| 4.7E-07 | NTI3606 | 402527 | 1044154 | 5.49E+02 | 5.49E+02 |
| 4.7E-07 | NTI4694 | 400115 | 1051304 | 9.27E+01 | 9.27E+01 |
| 4.7E-07 | NTI5372 | 404130 | 781344 | 1.41E+05 | 1.41E+05 |
| 4.7E-07 | NTI5384 | 413724 | 800956 | 3.16E+04 | 3.16E+04 |
| 4.7E-07 | NTI5410 | 400623 | 752036 | 4.01E+04 | 4.01E+04 |
| 4.7E-07 | NTI6225 | 413729 | 712931 | 7.69E+03 | 7.69E+03 |
| 4.7E-07 | NTI6320 | 415113 | 724159 | 9.45E+03 | 9.45E+03 |
| 4.7E-07 | NTI6332 | 414402 | 724326 | 1.86E+04 | 1.55E+05 |
| 4.7E-07 | NTI6596 | 321726 | 951515 | 5.79E+04 | 5.79E+04 |
| 4.7E-07 | NTI7024 | 412515 | 783409 | 7.26E+04 | 7.26E+04 |
| 4.7E-07 | NTI7025 | 413319 | 783500 | 7.18E+04 | 7.18E+04 |
| 4.7E-07 | NTI7026 | 412259 | 784600 | 1.51E+04 | 1.51E+04 |
| 4.7E-07 | NTI7049 | 285856 | 952036 | 6.60E+00 | 5.48E+01 |
| 4.7E-07 | NTI7150 | 294139 | 964724 | 2.64E+03 | 2.64E+03 |
| 4.7E-07 | NTI7172 | 395404 | 763744 | 5.87E+04 | 5.87E+04 |
| 4.7E-07 | NTI7194 | 400632 | 762839 | 1.16E+03 | 1.16E+03 |
| 4.7E-07 | NTI7203 | 411436 | 770221 | 5.48E+02 | 4.56E+03 |
| 4.7E-07 | NTI7288 | 402221 | 751755 | 3.40E+04 | 3.40E+04 |
| 4.7E-07 | NTI7323 | 400605 | 750820 | 2.82E+04 | 2.82E+04 |
| 4.7E-07 | NTI7345 | 401000 | 752016 | 1.78E+05 | 1.78E+05 |
| 4.7E-07 | NTI7347 | 401359 | 753310 | 1.77E+05 | 1.77E+05 |
| 4.7E-07 | NTI7348 | 401111 | 752611 | 1.89E+05 | 1.89E+05 |
| 4.7E-07 | NTI7350 | 401527 | 751945 | 9.43E+03 | 9.43E+03 |
| 4.7E-07 | NTI7365 | 401915 | 760133 | 3.37E+04 | 3.37E+04 |
| 4.7E-07 | NTI7367 | 401922 | 755628 | 3.21E+05 | 3.21E+05 |
| 4.7E-07 | NTI7368 | 402131 | 755615 | 1.65E+04 | 2.15E+04 |
| 4.7E-07 | NTI7418 | 322236 | 951640 | 3.83E+00 | 2.39E+01 |
| 4.7E-07 | NTI7573 | 325336 | 964210 | 5.49E+03 | 5.49E+03 |
| 4.7E-07 | NTI7752 | 313952 | 943946 | 1.38E+02 | 1.14E+03 |
| 4.7E-07 | NTI7803 | 330815 | 970243 | 1.28E+01 | 1.28E+01 |
| 4.7E-07 | NTI7925 | 325421 | 800559 | 1.46E+04 | 1.46E+04 |
| 4.7E-07 | NTI7956 | 345738 | 822631 | 1.33E+04 | 1.11E+05 |
| 4.7E-07 | NTI8273 | 301330 | 814013 | 7.46E+03 | 7.46E+03 |
| 4.7E-07 | NTI8297 | 281840 | 804233 | 9.19E+04 | 9.19E+04 |
| 4.7E-07 | NTI8346 | 291931 | 810656 | 1.65E+05 | 1.65E+05 |
| 4.7E-07 | NTI8448 | 340924 | 864950 | 2.58E+04 | 2.58E+04 |
| 4.7E-07 | NTI8534 | 343907 | 863950 | 1.89E+04 | 1.57E+05 |
| 4.7E-07 | NTI8573 | 333727 | 854451 | 4.73E+04 | 4.73E+04 |
| 4.7E-07 | NTI8604 | 303257 | 880814 | 2.16E+04 | 2.16E+04 |
| 4.7E-07 | NTI8637 | 292238 | 983402 | 8.83E+03 | 7.33E+04 |
| 4.7E-07 | NTI10887 | 324705 | 970258 | 4.92E+04 | 4.92E+04 |
| 4.7E-07 | NTI10900 | 350959 | 863357 | 1.24E+05 | 1.03E+06 |
| 4.7E-07 | NTI11106 | 334927 | 894754 | 3.64E+05 | 3.64E+05 |
| 4.7E-07 | NTI11217 | 285725 | 952316 | 1.09E+01 | 9.02E+01 |
| 4.7E-07 | NTI11248 | 381235 | 851335 | 2.70E+04 | 2.70E+04 |
| 4.7E-07 | NTI11259 | 374638 | 845110 | 1.28E+05 | 1.28E+05 |
| 4.7E-07 | NTI11295 | 285917 | 952304 | 3.81E+01 | 3.16E+02 |
| 4.7E-07 | NTI11307 | 390150 | 842641 | 4.08E+04 | 4.08E+04 |
| 4.7E-07 | NTI11344 | 364410 | 863344 | 9.26E+04 | 9.26E+04 |
| 4.7E-07 | NTI11368 | 374140 | 875228 | 1.51E+05 | 1.51E+05 |
| 4.7E-07 | NTI11648 | 395329 | 834330 | 2.42E+05 | 2.42E+05 |
| 4.7E-07 | NTI11698 | 400122 | 860006 | 5.10E+03 | 4.24E+04 |
| 4.7E-07 | NTI11809 | 325000 | 971905 | 2.53E+04 | 2.53E+04 |
| 4.7E-07 | NTI11837 | 422710 | 830530 | 1.93E+04 | 1.93E+04 |
| 4.7E-07 | NTI11865 | 421906 | 835317 | 7.08E+03 | 7.08E+03 |
| 4.7E-07 | NTI11916 | 425915 | 841257 | 7.88E+03 | 7.88E+03 |
| 4.7E-07 | NTI11917 | 425945 | 843500 | 6.80E+04 | 6.80E+04 |
| 4.7E-07 | NTI11984 | 431229 | 861457 | 5.48E+04 | 5.48E+04 |
| 4.7E-07 | NTI11985 | 431333 | 861243 | 3.88E+04 | 3.88E+04 |
| 4.7E-07 | NTI11994 | 425646 | 854060 | 1.54E+05 | 1.54E+05 |
| 4.7E-07 | NTI12011 | 441511 | 852518 | 2.41E+04 | 2.41E+04 |
| 4.7E-07 | NTI12015 | 294408 | 950528 | 2.86E+01 | 2.30E+02 |
| 4.7E-07 | NTI12294 | 295839 | 951633 | 1.47E+04 | 1.22E+05 |
| 4.7E-07 | NTI12320 | 445248 | 931219 | 9.21E+04 | 9.21E+04 |
| 4.7E-07 | NTI12333 | 445139 | 933130 | 5.33E+03 | 5.33E+03 |
| 4.7E-07 | NTI12350 | 445857 | 931306 | 3.96E+04 | 3.96E+04 |
| 4.7E-07 | NTI12355 | 450000 | 932137 | 4.39E+04 | 4.39E+04 |
| 4.7E-07 | NTI12371 | 325255 | 970253 | 1.65E+00 | 1.37E+01 |
| 4.7E-07 | NTI12393 | 433941 | 943014 | 6.03E+03 | 6.03E+03 |
| 4.7E-07 | NTI12595 | 324629 | 970334 | 5.21E+04 | 4.30E+05 |
| 4.7E-07 | NTI12689 | 383236 | 901944 | 4.57E+04 | 4.57E+04 |
| 4.7E-07 | NTI12749 | 371013 | 970140 | 2.63E+04 | 2.63E+04 |
| 4.7E-07 | NTI12925 | 353112 | 973830 | 6.64E+04 | 6.64E+04 |
| 4.7E-07 | NTI12974 | 362225 | 954947 | 8.40E+03 | 6.98E+04 |
| 4.7E-07 | NTI12985 | 345307 | 955656 | 5.48E+01 | 4.56E+02 |
| 4.7E-07 | NTI13146 | 393902 | 1050141 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NTI13238 | 294214 | 952353 | 1.37E-01 | 1.14E+00 |
| 4.7E-07 | NTI13336 | 453238 | 1222801 | 7.70E+03 | 6.40E+04 |
| 4.7E-07 | NTI18314 | 391913 | 762951 | 3.51E+03 | 3.51E+03 |
| 4.7E-07 | NTI18329 | 333815 | 855511 | 8.88E+04 | 8.88E+04 |
| 4.7E-07 | NTI18485 | 334430 | 1120030 | 1.40E+04 | 1.16E+05 |
| 4.7E-07 | NTI18497 | 332225 | 1114915 | 3.99E+01 | 3.99E+01 |
| 4.7E-07 | NTI18503 | 333110 | 1123700 | 1.60E+03 | 1.33E+04 |
| 4.7E-07 | NTI18505 | 333010 | 1123110 | 1.06E+03 | 8.81E+03 |
| 4.7E-07 | NTI18526 | 334210 | 1123720 | 1.22E+03 | 1.02E+04 |
| 4.7E-07 | NTI18533 | 332855 | 1115331 | 1.60E+02 | 1.60E+02 |
| 4.7E-07 | NTI18535 | 334640 | 1123030 | 1.36E+03 | 1.13E+04 |
| 4.7E-07 | NTI18551 | 332627 | 1120636 | 5.88E+00 | 4.89E+01 |
| 4.7E-07 | NTI18598 | 332739 | 1120618 | 9.59E+02 | 7.97E+03 |
| 4.7E-07 | NTI18603 | 333420 | 1123730 | 7.07E+02 | 5.87E+03 |
| 4.7E-07 | NTI18609 | 334210 | 1121000 | 6.88E+02 | 5.72E+03 |
| 4.7E-07 | NTI18760 | 374425 | 1221301 | 1.50E+01 | 1.50E+01 |
| 4.7E-07 | NTI18906 | 374047 | 1214550 | 4.01E+02 | 4.42E+02 |
| 4.7E-07 | NTI18907 | 374233 | 1215601 | 3.01E+03 | 3.01E+03 |
| 4.7E-07 | NTI19032 | 373837 | 1220803 | 1.55E+04 | 1.55E+04 |
| 4.7E-07 | NTI19036 | 372922 | 1215601 | 3.73E+00 | 3.73E+00 |
| 4.7E-07 | NTI19053 | 374626 | 1221502 | 8.82E+02 | 8.82E+02 |
| 4.7E-07 | NTI19090 | 375252 | 1221413 | 7.41E+00 | 7.41E+00 |
| 4.7E-07 | NTI19091 | 374134 | 1214302 | 1.13E+00 | 1.13E+00 |
| 4.7E-07 | NTI19927 | 363030 | 1193326 | 7.75E+01 | 7.75E+01 |
| 4.7E-07 | NTI20237 | 340758 | 1181608 | 1.53E+03 | 1.27E+04 |
| 4.7E-07 | NTI20243 | 340560 | 1181448 | 1.93E+03 | 1.93E+03 |
| 4.7E-07 | NTI20256 | 341347 | 1182204 | 3.70E+03 | 3.07E+04 |
| 4.7E-07 | NTI20272 | 335248 | 1180059 | 1.15E+04 | 9.58E+04 |
| 4.7E-07 | NTI20273 | 335624 | 1182503 | 2.69E+03 | 2.69E+03 |
| 4.7E-07 | NTI20276 | 341612 | 1182601 | 1.67E+03 | 1.39E+04 |
| 4.7E-07 | NTI20286 | 335548 | 1181006 | 1.11E+04 | 9.20E+04 |
| 4.7E-07 | NTI20317 | 340412 | 1181013 | 8.71E+03 | 7.24E+04 |
| 4.7E-07 | NTI20336 | 341018 | 1181925 | 6.12E+00 | 5.08E+01 |
| 4.7E-07 | NTI20337 | 341334 | 1182243 | 7.60E+02 | 7.60E+02 |
| 4.7E-07 | NTI20353 | 340147 | 1182626 | 1.20E+02 | 1.20E+02 |
| 4.7E-07 | NTI20357 | 340513 | 1180305 | 1.29E+02 | 1.29E+02 |
| 4.7E-07 | NTI20390 | 335601 | 1180416 | 3.77E+02 | 3.13E+03 |
| 4.7E-07 | NTI20411 | 340336 | 1181013 | 4.63E+02 | 4.63E+02 |
| 4.7E-07 | NTI20415 | 340224 | 1174727 | 5.48E+02 | 5.48E+02 |
| 4.7E-07 | NTI20508 | 340448 | 1181959 | 8.00E+03 | 6.65E+04 |
| 4.7E-07 | NTI20511 | 335623 | 1182542 | 1.29E+04 | 1.29E+04 |
| 4.7E-07 | NTI20517 | 335247 | 1181554 | 5.52E+03 | 4.59E+04 |
| 4.7E-07 | NTI20527 | 341123 | 1182044 | 1.73E+03 | 1.73E+03 |
| 4.7E-07 | NTI20533 | 340448 | 1180304 | 6.55E+02 | 6.55E+02 |
| 4.7E-07 | NTI20538 | 341433 | 1183546 | 5.00E+02 | 4.15E+03 |
| 4.7E-07 | NTI20553 | 335949 | 1175513 | 2.17E+02 | 2.17E+02 |
| 4.7E-07 | NTI20571 | 335454 | 1181832 | 2.35E+03 | 2.35E+03 |
| 4.7E-07 | NTI20588 | 335359 | 1181713 | 1.65E+03 | 1.37E+04 |
| 4.7E-07 | NTI20600 | 335345 | 1180256 | 8.27E+02 | 8.27E+02 |
| 4.7E-07 | NTI20605 | 335024 | 1181945 | 8.16E+02 | 8.16E+02 |
| 4.7E-07 | NTI20606 | 335053 | 1181356 | 1.49E+04 | 1.24E+05 |
| 4.7E-07 | NTI20617 | 340546 | 1180147 | 8.44E+02 | 4.88E+03 |
| 4.7E-07 | NTI20618 | 340824 | 1181647 | 2.37E+03 | 1.66E+04 |
| 4.7E-07 | NTI20675 | 340712 | 1181528 | 4.49E+01 | 4.49E+01 |
| 4.7E-07 | NTI20698 | 340534 | 1174334 | 3.02E+03 | 3.02E+03 |
| 4.7E-07 | NTI20749 | 334836 | 1180842 | 3.75E+02 | 3.75E+02 |
| 4.7E-07 | NTI20752 | 335359 | 1181634 | 8.16E+03 | 5.57E+04 |
| 4.7E-07 | NTI20758 | 340260 | 1174806 | 1.31E+04 | 1.31E+04 |
| 4.7E-07 | NTI20787 | 335457 | 1182343 | 2.00E+00 | 2.00E+00 |
| 4.7E-07 | NTI20827 | 335509 | 1182422 | 2.33E+03 | 1.94E+04 |
| 4.7E-07 | NTI20860 | 340001 | 1180419 | 1.34E+03 | 1.34E+03 |
| 4.7E-07 | NTI20861 | 335435 | 1180336 | 4.31E+03 | 4.31E+03 |
| 4.7E-07 | NTI20890 | 335527 | 1182619 | 9.53E+00 | 9.53E+00 |
| 4.7E-07 | NTI20904 | 340218 | 1181445 | 3.22E+01 | 3.22E+01 |
| 4.7E-07 | NTI20926 | 334629 | 1181548 | 2.90E+01 | 3.21E+01 |
| 4.7E-07 | NTI20940 | 340036 | 1175002 | 3.43E+01 | 3.43E+01 |
| 4.7E-07 | NTI20942 | 335237 | 1181357 | 2.50E+03 | 2.50E+03 |
| 4.7E-07 | NTI20950 | 335323 | 1181043 | 7.71E+03 | 6.40E+04 |
| 4.7E-07 | NTI20951 | 343453 | 1180802 | 1.27E-02 | 1.06E-01 |
| 4.7E-07 | NTI20955 | 334648 | 1180959 | 1.94E+01 | 1.94E+01 |
| 4.7E-07 | NTI20982 | 335020 | 1182024 | 4.76E+02 | 3.95E+03 |
| 4.7E-07 | NTI21018 | 335660 | 1180928 | 2.42E+03 | 2.01E+04 |
| 4.7E-07 | NTI21019 | 340803 | 1180031 | 4.94E+02 | 4.11E+03 |
| 4.7E-07 | NTI21020 | 334633 | 1181510 | 7.42E+01 | 6.16E+02 |
| 4.7E-07 | NTI21058 | 335024 | 1181355 | 9.98E+00 | 9.98E+00 |
| 4.7E-07 | NTI21071 | 341536 | 1183429 | 3.55E+01 | 3.55E+01 |
| 4.7E-07 | NTI21090 | 341423 | 1182403 | 5.44E+02 | 5.44E+02 |
| 4.7E-07 | NTI21108 | 335436 | 1181831 | 6.95E+02 | 5.77E+03 |
| 4.7E-07 | NTI21125 | 340036 | 1181601 | 1.17E+04 | 9.70E+04 |
| 4.7E-07 | NTI21153 | 340748 | 1175518 | 9.25E+01 | 7.69E+02 |
| 4.7E-07 | NTI21168 | 335956 | 1175355 | 7.77E+02 | 6.46E+03 |
| 4.7E-07 | NTI21181 | 335324 | 1180256 | 2.96E+04 | 2.46E+05 |
| 4.7E-07 | NTI21226 | 341212 | 1182439 | 7.59E+02 | 7.59E+02 |
| 4.7E-07 | NTI21235 | 340260 | 1175948 | 3.00E+02 | 3.00E+02 |
| 4.7E-07 | NTI21236 | 335947 | 1181718 | 3.62E+02 | 1.42E+03 |
| 4.7E-07 | NTI21249 | 340060 | 1180301 | 1.63E+01 | 1.35E+02 |
| 4.7E-07 | NTI21255 | 340759 | 1175518 | 2.65E+03 | 2.20E+04 |
| 4.7E-07 | NTI21267 | 335248 | 1181712 | 1.05E+03 | 8.72E+03 |
| 4.7E-07 | NTI21281 | 340134 | 1182232 | 1.83E+02 | 1.52E+03 |
| 4.7E-07 | NTI21282 | 341159 | 1182045 | 8.46E+03 | 7.03E+04 |
| 4.7E-07 | NTI21339 | 335848 | 1181521 | 3.05E+04 | 2.53E+05 |
| 4.7E-07 | NTI21350 | 335360 | 1181831 | 1.24E+03 | 4.80E+03 |
| 4.7E-07 | NTI21365 | 340112 | 1175829 | 8.86E+03 | 7.36E+04 |
| 4.7E-07 | NTI21378 | 340823 | 1182159 | 1.31E+04 | 1.09E+05 |
| 4.7E-07 | NTI21407 | 340112 | 1182743 | 3.16E+03 | 2.62E+04 |
| 4.7E-07 | NTI21429 | 340111 | 1181405 | 3.79E+01 | 3.15E+02 |
| 4.7E-07 | NTI21439 | 335624 | 1182503 | 1.81E+00 | 1.81E+00 |
| 4.7E-07 | NTI21445 | 335920 | 1181245 | 1.64E+03 | 1.64E+03 |
| 4.7E-07 | NTI21450 | 340636 | 1181448 | 1.34E+03 | 1.11E+04 |
| 4.7E-07 | NTI21463 | 340047 | 1175513 | 1.85E-01 | 1.54E+00 |
| 4.7E-07 | NTI21478 | 341212 | 1182400 | 4.70E+02 | 4.70E+02 |
| 4.7E-07 | NTI21499 | 334460 | 1181351 | 1.22E+02 | 1.01E+03 |
| 4.7E-07 | NTI21511 | 341816 | 1182801 | 7.69E+04 | 6.39E+05 |
| 4.7E-07 | NTI21516 | 334760 | 1181746 | 1.73E+03 | 1.73E+03 |
| 4.7E-07 | NTI21544 | 341634 | 1182602 | 4.01E+02 | 4.01E+02 |
| 4.7E-07 | NTI21573 | 335960 | 1180734 | 4.84E+01 | 4.02E+02 |
| 4.7E-07 | NTI21961 | 335136 | 1175350 | 2.46E+03 | 2.04E+04 |
| 4.7E-07 | NTI21991 | 334638 | 1180015 | 1.68E+04 | 1.40E+05 |
| 4.7E-07 | NTI22010 | 335241 | 1175351 | 2.24E-01 | 1.86E+00 |
| 4.7E-07 | NTI22045 | 334760 | 1175151 | 8.22E+00 | 6.83E+01 |
| 4.7E-07 | NTI22048 | 333803 | 1175617 | 2.54E+01 | 2.54E+01 |
| 4.7E-07 | NTI22066 | 334246 | 1175541 | 8.91E-01 | 7.40E+00 |
| 4.7E-07 | NTI22067 | 334432 | 1175817 | 1.03E+03 | 8.60E+03 |
| 4.7E-07 | NTI22117 | 335136 | 1175350 | 6.40E+02 | 6.40E+02 |
| 4.7E-07 | NTI22124 | 335044 | 1180018 | 6.74E+00 | 5.60E+01 |
| 4.7E-07 | NTI22126 | 334948 | 1175428 | 2.44E+04 | 2.03E+05 |
| 4.7E-07 | NTI22160 | 335146 | 1175350 | 8.19E+04 | 6.80E+05 |
| 4.7E-07 | NTI22176 | 334230 | 1175620 | 7.62E+03 | 7.62E+03 |
| 4.7E-07 | NTI22192 | 334012 | 1175029 | 3.41E+04 | 2.84E+05 |
| 4.7E-07 | NTI22207 | 334143 | 1174951 | 2.51E+01 | 2.51E+01 |
| 4.7E-07 | NTI22254 | 335140 | 1175153 | 2.75E+02 | 2.75E+02 |
| 4.7E-07 | NTI22255 | 334130 | 1175108 | 2.83E+02 | 2.83E+02 |
| 4.7E-07 | NTI22259 | 334312 | 1175109 | 3.24E+02 | 2.69E+03 |
| 4.7E-07 | NTI22260 | 334246 | 1175541 | 4.81E+02 | 4.81E+02 |
| 4.7E-07 | NTI22295 | 334347 | 1180210 | 3.36E+03 | 2.79E+04 |
| 4.7E-07 | NTI22323 | 334724 | 1175229 | 1.45E+01 | 1.45E+01 |
| 4.7E-07 | NTI22326 | 334759 | 1180331 | 8.67E+03 | 7.21E+04 |
| 4.7E-07 | NTI22366 | 334912 | 1171612 | 8.21E+01 | 8.21E+01 |
| 4.7E-07 | NTI22372 | 333902 | 1161129 | 1.35E+03 | 1.35E+03 |
| 4.7E-07 | NTI22375 | 335157 | 1171534 | 1.36E+00 | 1.13E+01 |
| 4.7E-07 | NTI22474 | 335324 | 1171455 | 7.37E+02 | 7.37E+02 |
| 4.7E-07 | NTI22485 | 383752 | 1211250 | 4.97E+03 | 7.52E+03 |
| 4.7E-07 | NTI22624 | 382655 | 1212752 | 6.82E+00 | 2.18E+01 |
| 4.7E-07 | NTI22632 | 383051 | 1212339 | 5.81E+02 | 5.81E+02 |
| 4.7E-07 | NTI22652 | 383541 | 1212945 | 8.00E+02 | 6.65E+03 |
| 4.7E-07 | NTI22744 | 340412 | 1173033 | 2.08E+03 | 2.08E+03 |
| 4.7E-07 | NTI22848 | 353858 | 1173149 | 5.39E+02 | 5.39E+02 |
| 4.7E-07 | NTI22907 | 340328 | 1174136 | 4.49E+01 | 4.49E+01 |
| 4.7E-07 | NTI22939 | 341352 | 1160320 | 3.12E+01 | 2.59E+02 |
| 4.7E-07 | NTI22940 | 345230 | 1165445 | 1.51E+02 | 1.25E+03 |
| 4.7E-07 | NTI22941 | 345256 | 1165307 | 5.78E+04 | 4.79E+05 |
| 4.7E-07 | NTI22952 | 340533 | 1173822 | 5.76E+04 | 4.78E+05 |
| 4.7E-07 | NTI23064 | 324916 | 1170832 | 7.78E-02 | 4.85E-01 |
| 4.7E-07 | NTI23077 | 324127 | 1170758 | 1.56E+01 | 1.21E+02 |
| 4.7E-07 | NTI23188 | 331908 | 1172221 | 2.87E+01 | 1.79E+02 |
| 4.7E-07 | NTI23514 | 374613 | 1222556 | 6.29E+01 | 5.23E+02 |
| 4.7E-07 | NTI24080 | 373401 | 1221915 | 4.84E+02 | 4.84E+02 |
| 4.7E-07 | NTI24426 | 342552 | 1195223 | 1.98E+02 | 1.98E+02 |
| 4.7E-07 | NTI24427 | 345521 | 1202737 | 9.23E+01 | 6.38E+02 |
| 4.7E-07 | NTI24430 | 342552 | 1195223 | 2.36E+02 | 2.36E+02 |
| 4.7E-07 | NTI24529 | 372138 | 1215417 | 4.52E+01 | 4.52E+01 |
| 4.7E-07 | NTI24755 | 372145 | 1215657 | 5.12E+02 | 4.26E+03 |
| 4.7E-07 | NTI24823 | 371206 | 1214942 | 6.01E+00 | 6.01E+00 |
| 4.7E-07 | NTI24980 | 372320 | 1220628 | 5.02E-01 | 5.02E-01 |
| 4.7E-07 | NTI25016 | 371630 | 1215704 | 8.24E+02 | 8.24E+02 |
| 4.7E-07 | NTI25038 | 372437 | 1215339 | 1.29E+03 | 1.29E+03 |
| 4.7E-07 | NTI25245 | 372235 | 1220143 | 1.50E+02 | 1.50E+02 |
| 4.7E-07 | NTI25296 | 372354 | 1220910 | 2.52E+00 | 2.52E+00 |
| 4.7E-07 | NTI25515 | 381447 | 1215736 | 4.11E+01 | 4.11E+01 |
| 4.7E-07 | NTI25756 | 382552 | 1224249 | 5.53E+01 | 5.53E+01 |
| 4.7E-07 | NTI25972 | 340948 | 1191326 | 1.76E+00 | 1.41E+01 |
| 4.7E-07 | NTI25980 | 341459 | 1191334 | 5.29E+02 | 5.29E+02 |
| 4.7E-07 | NTI25984 | 340849 | 1191048 | 6.32E+01 | 6.32E+01 |
| 4.7E-07 | NTI26014 | 340842 | 1191127 | 2.25E+01 | 2.25E+01 |
| 4.7E-07 | NTI26038 | 341611 | 1184219 | 2.49E+01 | 2.49E+01 |
| 4.7E-07 | NTI26060 | 341451 | 1184059 | 1.46E+04 | 1.46E+04 |
| 4.7E-07 | NTI26095 | 341015 | 1190932 | 5.34E+00 | 4.44E+01 |
| 4.7E-07 | NTI26183 | 390710 | 753400 | 3.55E+04 | 3.55E+04 |
| 4.7E-07 | NTI31360 | 390201 | 845804 | 1.31E+04 | 1.31E+04 |
| 4.7E-07 | NTI31387 | 412518 | 845146 | 3.12E+03 | 3.12E+03 |
| 4.7E-07 | NTI31541 | 414026 | 855853 | 4.06E+05 | 4.06E+05 |
| 4.7E-07 | NTI32072 | 394401 | 861240 | 3.43E+03 | 2.85E+04 |
| 4.7E-07 | NTI32786 | 390126 | 944251 | 2.06E+04 | 1.71E+05 |
| 4.7E-07 | NTI32829 | 373951 | 972300 | 5.28E+04 | 5.28E+04 |
| 4.7E-07 | NTI32831 | 373728 | 971650 | 5.95E+05 | 2.63E+06 |
| 4.7E-07 | NTI32837 | 374116 | 972327 | 4.97E+04 | 4.97E+04 |
| 4.7E-07 | NTI32838 | 374138 | 971327 | 1.31E+03 | 1.31E+03 |
| 4.7E-07 | NTI33916 | 425238 | 853403 | 7.15E+03 | 7.15E+03 |
| 4.7E-07 | NTI34114 | 385823 | 921819 | 6.57E+03 | 6.57E+03 |
| 4.7E-07 | NTI34145 | 380000 | 924500 | 1.97E+04 | 1.97E+04 |
| 4.7E-07 | NTI34209 | 385700 | 924360 | 3.59E+04 | 3.59E+04 |
| 4.7E-07 | NTI34210 | 385843 | 925834 | 1.25E+05 | 1.25E+05 |
| 4.7E-07 | NTI34330 | 390836 | 943048 | 2.68E+01 | 2.68E+01 |
| 4.7E-07 | NTI34331 | 385612 | 942328 | 1.06E+03 | 1.06E+03 |
| 4.7E-07 | NTI34373 | 385248 | 943133 | 1.15E+04 | 1.15E+04 |
| 4.7E-07 | NTI34377 | 385728 | 943431 | 3.69E+04 | 4.01E+04 |
| 4.7E-07 | NTI34385 | 374556 | 943138 | 1.93E+04 | 1.93E+04 |
| 4.7E-07 | NTI34395 | 370337 | 942813 | 3.93E+02 | 3.93E+02 |
| 4.7E-07 | NTI34460 | 385151 | 911942 | 2.96E+04 | 2.96E+04 |
| 4.7E-07 | NTI34472 | 360258 | 942130 | 1.34E+04 | 1.11E+05 |
| 4.7E-07 | NTI34514 | 391742 | 944143 | 1.15E+05 | 9.57E+05 |
| 4.7E-07 | NTI34574 | 383343 | 902736 | 3.36E+03 | 2.79E+04 |
| 4.7E-07 | NTI34595 | 383307 | 902738 | 9.22E+02 | 9.22E+02 |
| 4.7E-07 | NTI34673 | 383636 | 902008 | 1.19E+04 | 9.92E+04 |
| 4.7E-07 | NTI34682 | 384436 | 902224 | 1.48E+03 | 1.48E+03 |
| 4.7E-07 | NTI34749 | 383728 | 901729 | 1.53E+04 | 1.53E+04 |
| 4.7E-07 | NTI34765 | 383745 | 901222 | 5.23E+02 | 5.23E+02 |
| 4.7E-07 | NTI34784 | 383427 | 901358 | 6.34E+01 | 5.27E+02 |
| 4.7E-07 | NTI34802 | 383536 | 901536 | 4.85E+04 | 4.85E+04 |
| 4.7E-07 | NTI35353 | 420838 | 760244 | 1.09E+03 | 9.07E+03 |
| 4.7E-07 | NTI35612 | 421832 | 752351 | 4.18E+03 | 4.18E+03 |
| 4.7E-07 | NTI36095 | 404008 | 735420 | 4.10E+04 | 4.10E+04 |
| 4.7E-07 | NTI37024 | 430909 | 774420 | 3.45E+04 | 3.45E+04 |
| 4.7E-07 | NTI38194 | 430618 | 751249 | 7.36E+04 | 7.36E+04 |
| 4.7E-07 | NTI38195 | 430519 | 751502 | 5.46E+04 | 5.46E+04 |
| 4.7E-07 | NTI39761 | 404212 | 732246 | 4.11E+03 | 3.42E+04 |
| 4.7E-07 | NTI40416 | 412448 | 814707 | 4.25E+04 | 3.53E+05 |
| 4.7E-07 | NTI40507 | 410822 | 812836 | 1.08E+05 | 1.08E+05 |
| 4.7E-07 | NTI41338 | 344114 | 821358 | 1.45E+03 | 1.45E+03 |
| 4.7E-07 | NTI41417 | 344605 | 830152 | 7.71E+03 | 7.71E+03 |
| 4.7E-07 | NTI41653 | 325118 | 965150 | 5.65E+03 | 5.65E+03 |
| 4.7E-07 | NTI42445 | 393336 | 785006 | 2.79E+03 | 2.79E+03 |
| 4.7E-07 | NTI42595 | 431128 | 884351 | 2.99E+03 | 2.99E+03 |
| 4.7E-07 | NTI42671 | 440449 | 874210 | 8.30E+04 | 8.30E+04 |
| 4.7E-07 | NTI42701 | 445338 | 875344 | 2.63E+04 | 2.63E+04 |
| 4.7E-07 | NTI42711 | 431905 | 875733 | 1.43E+04 | 1.43E+04 |
| 4.7E-07 | NTI42750 | 424337 | 874727 | 1.08E+04 | 1.08E+04 |
| 4.7E-07 | NTI43004 | 433755 | 884405 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NTI43015 | 434657 | 882702 | 8.88E+03 | 8.88E+03 |
| 4.7E-07 | NTI43378 | 360713 | 864136 | 6.42E+04 | 6.42E+04 |
| 4.7E-07 | NTI44511 | 451249 | 932441 | 1.67E+04 | 1.67E+04 |
| 4.7E-07 | NTI44700 | 351908 | 783718 | 1.16E+03 | 1.16E+03 |
| 4.7E-07 | NTI44730 | 445454 | 932456 | 8.99E+03 | 8.99E+03 |
| 4.7E-07 | NTI44831 | 354136 | 811058 | 2.89E+01 | 2.89E+01 |
| 4.7E-07 | NTI45064 | 350859 | 790008 | 7.37E+01 | 2.74E+02 |
| 4.7E-07 | NTI45127 | 414700 | 713104 | 7.28E+03 | 7.28E+03 |
| 4.7E-07 | NTI45263 | 415225 | 712436 | 2.80E+04 | 2.80E+04 |
| 4.7E-07 | NTI45366 | 353902 | 802941 | 7.54E+02 | 6.26E+03 |
| 4.7E-07 | NTI45427 | 341913 | 784422 | 3.65E+04 | 3.65E+04 |
| 4.7E-07 | NTI45456 | 445921 | 931525 | 8.35E+03 | 8.35E+03 |
| 4.7E-07 | NTI46048 | 354618 | 783259 | 2.22E+03 | 1.84E+04 |
| 4.7E-07 | NTI46604 | 473906 | 1222109 | 2.45E+04 | 2.45E+04 |
| 4.7E-07 | NTI46675 | 474008 | 1221143 | 7.83E+04 | 7.83E+04 |
| 4.7E-07 | NTI47980 | 414319 | 874133 | 1.78E-01 | 1.48E+00 |
| 4.7E-07 | NTI48022 | 415624 | 875237 | 2.39E+04 | 2.39E+04 |
| 4.7E-07 | NTI48035 | 415627 | 875309 | 2.35E+04 | 2.35E+04 |
| 4.7E-07 | NTI48062 | 415703 | 875319 | 2.89E+03 | 2.89E+03 |
| 4.7E-07 | NTI48274 | 420104 | 874716 | 7.53E+03 | 7.53E+03 |
| 4.7E-07 | NTI48296 | 420204 | 875346 | 1.34E+04 | 1.34E+04 |
| 4.7E-07 | NTI48419 | 420119 | 875750 | 5.62E+03 | 4.67E+04 |
| 4.7E-07 | NTI48445 | 415757 | 875222 | 8.68E+03 | 8.68E+03 |
| 4.7E-07 | NTI48447 | 415808 | 875150 | 8.52E+04 | 1.69E+05 |
| 4.7E-07 | NTI48500 | 420052 | 874321 | 1.70E+04 | 1.70E+04 |
| 4.7E-07 | NTI48613 | 415917 | 880958 | 9.73E+04 | 9.73E+04 |
| 4.7E-07 | NTI48676 | 420014 | 875752 | 9.45E+04 | 4.15E+05 |
| 4.7E-07 | NTI48732 | 415617 | 874127 | 9.43E+02 | 9.43E+02 |
| 4.7E-07 | NTI48889 | 415626 | 874135 | 8.11E+03 | 8.11E+03 |
| 4.7E-07 | NTI48996 | 415701 | 874127 | 1.22E+04 | 1.22E+04 |
| 4.7E-07 | NTI49452 | 415116 | 873854 | 1.99E+04 | 1.99E+04 |
| 4.7E-07 | NTI49525 | 415544 | 874354 | 3.54E+04 | 3.54E+04 |
| 4.7E-07 | NTI49526 | 414820 | 874232 | 8.03E+04 | 8.03E+04 |
| 4.7E-07 | NTI49625 | 415109 | 874413 | 5.98E+04 | 5.98E+04 |
| 4.7E-07 | NTI50167 | 414420 | 875615 | 3.48E+04 | 3.48E+04 |
| 4.7E-07 | NTI51064 | 414018 | 883215 | 2.37E+04 | 2.37E+04 |
| 4.7E-07 | NTI51145 | 422248 | 875400 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NTI51298 | 420924 | 880813 | 2.42E+04 | 2.42E+04 |
| 4.7E-07 | NTI51726 | 421441 | 881912 | 4.01E+03 | 4.01E+03 |
| 4.7E-07 | NTI51753 | 421030 | 882543 | 3.35E+03 | 3.35E+03 |
| 4.7E-07 | NTI51843 | 421507 | 883644 | 2.95E+03 | 2.45E+04 |
| 4.7E-07 | NTI52191 | 384015 | 901040 | 1.93E+03 | 1.93E+03 |
| 4.7E-07 | NTI52497 | 420759 | 891503 | 2.91E+05 | 2.91E+05 |
| 4.7E-07 | NTI53014 | 383534 | 901031 | 1.76E+05 | 1.76E+05 |
| 4.7E-07 | NTI53352 | 400837 | 873547 | 5.33E+03 | 4.43E+04 |
| 4.7E-07 | NTI53562 | 413739 | 895714 | 1.34E+04 | 1.34E+04 |
| 4.7E-07 | NTI53688 | 413842 | 874130 | 2.99E+04 | 2.99E+04 |
| 4.7E-07 | NTI53869 | 421542 | 890543 | 2.45E+04 | 2.45E+04 |
| 4.7E-07 | NTI54284 | 472933 | 1221232 | 9.53E+00 | 9.53E+00 |
| 4.7E-07 | NTI54795 | 415657 | 875207 | 1.66E+04 | 1.66E+04 |
| 4.7E-07 | NTI54855 | 420120 | 875740 | 1.91E+04 | 1.91E+04 |
| 4.7E-07 | NTI54879 | 415856 | 874660 | 1.15E+04 | 1.15E+04 |
| 4.7E-07 | NTI54963 | 415508 | 873947 | 1.98E+04 | 1.98E+04 |
| 4.7E-07 | NTI55239 | 414760 | 880400 | 2.91E+04 | 2.91E+04 |
| 4.7E-07 | NTI55477 | 415450 | 881641 | 3.93E+04 | 3.93E+04 |
| 4.7E-07 | NTI55719 | 422618 | 881459 | 1.07E+05 | 1.07E+05 |
| 4.7E-07 | NTI55774 | 394914 | 885755 | 8.87E+04 | 4.27E+05 |
| 4.7E-07 | NTI56136 | 421803 | 893654 | 1.92E+04 | 1.92E+04 |
| 4.7E-07 | NTI56886 | 431044 | 851426 | 8.52E+02 | 8.52E+02 |
| 4.7E-07 | NTI57049 | 350340 | 851627 | 8.16E+02 | 8.16E+02 |
| 4.7E-07 | NTIAL0450008 | 311958 | 854226 | 2.19E+02 | 1.82E+03 |
| 4.7E-07 | NTICA00160 | 374421 | 1221306 | 4.50E+03 | 4.50E+03 |
| 4.7E-07 | NTICA0371157 | 340260 | 1181406 | 3.08E+01 | 3.08E+01 |
| 4.7E-07 | NTICA0371160 | 335248 | 1180138 | 1.90E+03 | 1.90E+03 |
| 4.7E-07 | NTICA0371195 | 340860 | 1181924 | 3.48E+02 | 3.48E+02 |
| 4.7E-07 | NTICA0371208 | 334904 | 1181119 | 8.97E+01 | 7.45E+02 |
| 4.7E-07 | NTICA0371215 | 335654 | 1180353 | 1.10E+03 | 1.10E+03 |
| 4.7E-07 | NTICA0371244 | 341256 | 1183539 | 1.15E+03 | 1.15E+03 |
| 4.7E-07 | NTICA0371308 | 340260 | 1181406 | 4.17E+01 | 4.17E+01 |
| 4.7E-07 | NTICA0371319 | 340224 | 1180854 | 4.17E-01 | 4.17E-01 |
| 4.7E-07 | NTICA0371347 | 335955 | 1181915 | 3.27E+01 | 3.27E+01 |
| 4.7E-07 | NTICA0371361 | 335552 | 1182507 | 2.55E+03 | 2.55E+03 |
| 4.7E-07 | NTICA0371364 | 335259 | 1180053 | 3.43E+02 | 3.43E+02 |
| 4.7E-07 | NTICA0371369 | 335548 | 1180730 | 2.24E+03 | 2.24E+03 |
| 4.7E-07 | NTICA0371372 | 341035 | 1181846 | 1.89E+02 | 1.89E+02 |
| 4.7E-07 | NTICA0371378 | 335950 | 1181245 | 1.61E+03 | 1.61E+03 |
| 4.7E-07 | NTICA0371392 | 335135 | 1180924 | 1.44E+02 | 1.20E+03 |
| 4.7E-07 | NTICA0371508 | 341042 | 1183521 | 8.11E+03 | 6.74E+04 |
| 4.7E-07 | NTICA0371551 | 335336 | 1180154 | 3.43E+02 | 3.43E+02 |
| 4.7E-07 | NTICA0371606 | 335547 | 1182344 | 3.54E+02 | 3.54E+02 |
| 4.7E-07 | NTICA0378 | 340738 | 1175540 | 1.28E+04 | 1.28E+04 |
| 4.7E-07 | NTICA0531869 | 364820 | 1214722 | 1.40E+03 | 1.40E+03 |
| 4.7E-07 | NTICA0592053 | 334200 | 1175109 | 4.10E+03 | 4.10E+03 |
| 4.7E-07 | NTICA0592066 | 335132 | 1175011 | 2.58E+03 | 2.58E+03 |
| 4.7E-07 | NTICA0592131 | 334312 | 1174952 | 2.93E+04 | 1.79E+05 |
| 4.7E-07 | NTICA0672219 | 383039 | 1212251 | 1.77E+03 | 1.77E+03 |
| 4.7E-07 | NTICA0712392 | 345329 | 1165243 | 9.59E+00 | 7.97E+01 |
| 4.7E-07 | NTICA0712501 | 340524 | 1173625 | 5.44E+03 | 5.44E+03 |
| 4.7E-07 | NTICA0732595 | 324928 | 1170925 | 1.92E+00 | 1.20E+01 |
| 4.7E-07 | NTICA0732603 | 323748 | 1170623 | 4.23E-01 | 2.64E+00 |
| 4.7E-07 | NTICA0732639 | 324845 | 1171300 | 1.56E-01 | 1.30E+00 |
| 4.7E-07 | NTICA0732675 | 330819 | 1171309 | 9.26E+02 | 7.70E+03 |
| 4.7E-07 | NTICA0732740 | 324157 | 1171211 | 9.63E+03 | 9.68E+03 |
| 4.7E-07 | NTICA0732742 | 323922 | 1170605 | 1.84E-01 | 1.53E+00 |
| 4.7E-07 | NTICA0732754 | 325630 | 1170220 | 1.33E+03 | 1.33E+03 |
| 4.7E-07 | NTICA0732901 | 324830 | 1165801 | 3.60E+03 | 3.60E+03 |
| 4.7E-07 | NTICA0732960 | 324905 | 1165843 | 2.42E+03 | 2.01E+04 |
| 4.7E-07 | NTICA0732967 | 331248 | 1172340 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NTICA0732968 | 324143 | 1170819 | 2.10E-01 | 1.31E+00 |
| 4.7E-07 | NTICA0732973 | 330609 | 1171305 | 2.69E+02 | 2.92E+02 |
| 4.7E-07 | NTICA0732981 | 324934 | 1165912 | 1.84E+03 | 1.53E+04 |
| 4.7E-07 | NTICA0732984 | 330854 | 1171258 | 2.32E+02 | 1.92E+03 |
| 4.7E-07 | NTICA0733011 | 324126 | 1170714 | 5.34E-01 | 4.43E+00 |
| 4.7E-07 | NTICA0733188 | 323554 | 1170452 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NTICA0733201 | 325254 | 1170756 | 1.11E+01 | 6.94E+01 |
| 4.7E-07 | NTICA0733205 | 324050 | 1170726 | 1.09E+01 | 6.78E+01 |
| 4.7E-07 | NTICA0733211 | 324327 | 1171255 | 1.82E+00 | 1.51E+01 |
| 4.7E-07 | NTICA0733419 | 323445 | 1170660 | 1.17E+00 | 7.30E+00 |
| 4.7E-07 | NTICA0733422 | 325113 | 1165812 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NTICA0733441 | 324622 | 1170417 | 2.10E+01 | 1.42E+02 |
| 4.7E-07 | NTICA0773887 | 374317 | 1212852 | 1.92E-01 | 1.59E+00 |
| 4.7E-07 | NTICA0834297 | 342553 | 1195223 | 3.32E+02 | 2.52E+03 |
| 4.7E-07 | NTICA0834308 | 342555 | 1195201 | 4.03E+01 | 4.03E+01 |
| 4.7E-07 | NTICA0854685 | 372505 | 1220909 | 9.42E+01 | 9.42E+01 |
| 4.7E-07 | NTICA0854805 | 372229 | 1215538 | 5.52E+01 | 5.52E+01 |
| 4.7E-07 | NTICA0854846 | 372314 | 1215457 | 3.63E+02 | 3.63E+02 |
| 4.7E-07 | NTICA0955098 | 381621 | 1215907 | 6.42E+03 | 6.42E+03 |
| 4.7E-07 | NTICA1014302 | 363042 | 1193254 | 1.64E+00 | 8.85E+00 |
| 4.7E-07 | NTICA1115531 | 340637 | 1190650 | 7.66E+01 | 7.66E+01 |
| 4.7E-07 | NTICA1115644 | 341122 | 1191013 | 5.05E+01 | 5.05E+01 |
| 4.7E-07 | NTICA1115692 | 341617 | 1184337 | 5.00E+00 | 4.16E+01 |
| 4.7E-07 | NTICA1115697 | 341643 | 1185442 | 8.91E-02 | 7.40E-01 |
| 4.7E-07 | NTICA1505123 | 353721 | 1174053 | 1.22E+01 | 1.22E+01 |
| 4.7E-07 | NTICAT$12604 | 335512 | 1182305 | 9.98E+03 | 1.03E+04 |
| 4.7E-07 | NTICO0048 | 381413 | 1043646 | 5.62E+01 | 4.67E+02 |
| 4.7E-07 | NTICO0050996 | 393718 | 1045914 | 5.18E+01 | 5.18E+01 |
| 4.7E-07 | NTICO0130615 | 400413 | 1051216 | 3.47E+03 | 3.47E+03 |
| 4.7E-07 | NTICO0310511 | 394233 | 1045927 | 7.60E+02 | 6.32E+03 |
| 4.7E-07 | NTICO0632 | 400903 | 1050116 | 1.93E+03 | 1.93E+03 |
| 4.7E-07 | NTICO1819 | 395019 | 1043959 | 1.53E+03 | 1.53E+03 |
| 4.7E-07 | NTICTT$579 | 412730 | 724100 | 1.26E+05 | 1.26E+05 |
| 4.7E-07 | NTICTT$610 | 412715 | 724945 | 5.55E+04 | 4.61E+05 |
| 4.7E-07 | NTIFL0090132 | 280304 | 803622 | 8.98E+02 | 8.98E+02 |
| 4.7E-07 | NTIFL0250827 | 255536 | 801522 | 7.99E+04 | 7.99E+04 |
| 4.7E-07 | NTIFL0571103 | 275655 | 822729 | 2.59E+03 | 2.59E+03 |
| 4.7E-07 | NTIFL0610023 | 273917 | 802458 | 7.89E+03 | 7.89E+03 |
| 4.7E-07 | NTIFL1010335 | 281628 | 823821 | 4.94E+03 | 4.94E+03 |
| 4.7E-07 | NTIFL1030098 | 274856 | 824504 | 1.03E+03 | 1.03E+03 |
| 4.7E-07 | NTIFL1030416 | 275211 | 824303 | 3.04E+04 | 3.04E+04 |
| 4.7E-07 | NTIFLR023003 | 301029 | 823431 | 7.26E+01 | 7.26E+01 |
| 4.7E-07 | NTIFLR083013 | 291305 | 820835 | 9.07E+00 | 9.07E+00 |
| 4.7E-07 | NTIIL0075859 | 421504 | 885234 | 3.65E+02 | 3.03E+03 |
| 4.7E-07 | NTIIL011100A | 412014 | 891309 | 1.85E+04 | 1.85E+04 |
| 4.7E-07 | NTIIL0115886 | 412315 | 892726 | 1.48E+04 | 1.48E+04 |
| 4.7E-07 | NTIIL0195954 | 401641 | 882302 | 8.03E+03 | 8.03E+03 |
| 4.7E-07 | NTIIL031195A | 420135 | 874715 | 6.21E+04 | 6.21E+04 |
| 4.7E-07 | NTIIL03142 | 420108 | 874735 | 2.60E+04 | 2.60E+04 |
| 4.7E-07 | NTIIL0316063 | 414748 | 875140 | 5.99E+03 | 4.97E+04 |
| 4.7E-07 | NTIIL0316147 | 415628 | 875123 | 2.23E+02 | 1.85E+03 |
| 4.7E-07 | NTIIL0316332 | 415118 | 875127 | 3.21E+04 | 3.21E+04 |
| 4.7E-07 | NTIIL0316389 | 415212 | 875150 | 6.08E+04 | 6.08E+04 |
| 4.7E-07 | NTIIL0316435 | 420040 | 874316 | 8.16E+03 | 8.16E+03 |
| 4.7E-07 | NTIIL0316449 | 414819 | 875125 | 2.32E+02 | 2.32E+02 |
| 4.7E-07 | NTIIL0316467 | 420223 | 874737 | 3.39E+04 | 3.39E+04 |
| 4.7E-07 | NTIIL0316485 | 415437 | 875317 | 5.00E+03 | 1.22E+04 |
| 4.7E-07 | NTIIL0316542 | 414909 | 875147 | 2.09E+03 | 2.09E+03 |
| 4.7E-07 | NTIIL0316594 | 415659 | 875149 | 6.27E+04 | 6.27E+04 |
| 4.7E-07 | NTIIL0316611 | 415831 | 875160 | 1.20E+04 | 1.20E+04 |
| 4.7E-07 | NTIIL0316639 | 420134 | 874254 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NTIIL0316641 | 420108 | 874308 | 1.47E+04 | 1.47E+04 |
| 4.7E-07 | NTIIL0316669 | 420051 | 874313 | 9.79E+03 | 8.14E+04 |
| 4.7E-07 | NTIIL0316674 | 420137 | 874319 | 6.40E+03 | 6.40E+03 |
| 4.7E-07 | NTIIL0316686 | 420844 | 875111 | 6.53E+03 | 6.53E+03 |
| 4.7E-07 | NTIIL0316702 | 420108 | 874707 | 4.72E+02 | 4.72E+02 |
| 4.7E-07 | NTIIL0316720 | 420108 | 874652 | 7.41E+03 | 7.41E+03 |
| 4.7E-07 | NTIIL0316721 | 420058 | 874655 | 3.01E+03 | 3.01E+03 |
| 4.7E-07 | NTIIL0316723 | 415518 | 881815 | 4.10E+03 | 3.41E+04 |
| 4.7E-07 | NTIIL0316747 | 415530 | 875020 | 7.72E+02 | 7.72E+02 |
| 4.7E-07 | NTIIL0316811 | 413422 | 873648 | 4.82E+03 | 4.82E+03 |
| 4.7E-07 | NTIIL0316822 | 420738 | 875514 | 5.41E+03 | 5.41E+03 |
| 4.7E-07 | NTIIL0316841 | 420147 | 875848 | 4.01E+03 | 4.01E+03 |
| 4.7E-07 | NTIIL0316842 | 420011 | 880027 | 9.20E+04 | 9.20E+04 |
| 4.7E-07 | NTIIL0316873 | 415358 | 875357 | 5.42E+04 | 5.42E+04 |
| 4.7E-07 | NTIIL0316967 | 415606 | 874136 | 1.61E+04 | 1.61E+04 |
| 4.7E-07 | NTIIL0316985 | 415645 | 874259 | 3.89E+02 | 3.89E+02 |
| 4.7E-07 | NTIIL0316995 | 415302 | 873858 | 3.43E+00 | 2.85E+01 |
| 4.7E-07 | NTIIL0317020 | 414826 | 874157 | 1.20E+04 | 9.95E+04 |
| 4.7E-07 | NTIIL0317139 | 415316 | 874002 | 8.27E+03 | 8.27E+03 |
| 4.7E-07 | NTIIL0317140 | 415249 | 873927 | 1.37E+03 | 1.37E+03 |
| 4.7E-07 | NTIIL0317197 | 415547 | 874031 | 8.51E+03 | 8.51E+03 |
| 4.7E-07 | NTIIL0317202 | 415734 | 874028 | 2.07E+02 | 2.07E+02 |
| 4.7E-07 | NTIIL0317290 | 415612 | 874110 | 1.11E+04 | 1.11E+04 |
| 4.7E-07 | NTIIL0317360 | 415308 | 874003 | 3.01E+04 | 3.01E+04 |
| 4.7E-07 | NTIIL0317512 | 414930 | 874009 | 5.48E+03 | 4.56E+04 |
| 4.7E-07 | NTIIL0317662 | 415454 | 874420 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NTIIL0317669 | 415620 | 874117 | 1.47E+04 | 1.47E+04 |
| 4.7E-07 | NTIIL0317689 | 415853 | 874538 | 2.61E+04 | 2.61E+04 |
| 4.7E-07 | NTIIL0317835 | 415714 | 875213 | 2.85E+03 | 2.37E+04 |
| 4.7E-07 | NTIIL043020A | 415418 | 880607 | 8.81E+04 | 8.81E+04 |
| 4.7E-07 | NTIIL043095A | 414760 | 875800 | 2.55E+04 | 2.55E+04 |
| 4.7E-07 | NTIIL0437946 | 415530 | 880507 | 2.49E+03 | 2.49E+03 |
| 4.7E-07 | NTIIL0437960 | 414827 | 880255 | 6.17E+04 | 6.17E+04 |
| 4.7E-07 | NTIIL0437995 | 415436 | 875826 | 4.34E+03 | 4.34E+03 |
| 4.7E-07 | NTIIL0438058 | 414760 | 880230 | 1.43E+03 | 1.18E+04 |
| 4.7E-07 | NTIIL0438061 | 415343 | 880722 | 2.32E+04 | 2.32E+04 |
| 4.7E-07 | NTIIL0438066 | 414628 | 880232 | 7.72E+03 | 7.72E+03 |
| 4.7E-07 | NTIIL0438067 | 415418 | 880558 | 1.93E+04 | 1.93E+04 |
| 4.7E-07 | NTIIL0438068 | 414734 | 880215 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NTIIL0438073 | 414730 | 880230 | 1.22E+03 | 1.01E+04 |
| 4.7E-07 | NTIIL0438080 | 415837 | 875913 | 3.61E+02 | 3.61E+02 |
| 4.7E-07 | NTIIL0438118 | 415816 | 875633 | 1.35E+04 | 1.35E+04 |
| 4.7E-07 | NTIIL0458147 | 393556 | 874137 | 9.96E+03 | 8.28E+04 |
| 4.7E-07 | NTIIL0638273 | 412260 | 882500 | 1.98E+03 | 1.65E+04 |
| 4.7E-07 | NTIIL089080A | 415946 | 881735 | 3.47E+04 | 3.47E+04 |
| 4.7E-07 | NTIIL0898406 | 414522 | 882626 | 3.18E+02 | 3.18E+02 |
| 4.7E-07 | NTIIL0898477 | 420423 | 881746 | 8.01E+03 | 8.01E+03 |
| 4.7E-07 | NTIIL0978631 | 421134 | 880700 | 2.43E+04 | 2.43E+04 |
| 4.7E-07 | NTIIL0978698 | 422150 | 874960 | 2.22E+03 | 1.84E+04 |
| 4.7E-07 | NTIIL0978727 | 421532 | 875913 | 1.45E+04 | 1.45E+04 |
| 4.7E-07 | NTIIL0998825 | 410737 | 884753 | 1.08E+04 | 1.08E+04 |
| 4.7E-07 | NTIIL111005A | 421013 | 881756 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NTIIL1118956 | 422850 | 881833 | 1.01E+04 | 1.01E+04 |
| 4.7E-07 | NTIIL1118985 | 421205 | 881410 | 2.04E+03 | 1.69E+04 |
| 4.7E-07 | NTIIL1118996 | 421454 | 881837 | 3.96E+03 | 3.96E+03 |
| 4.7E-07 | NTIIL1118997 | 421211 | 882104 | 6.68E+01 | 5.55E+02 |
| 4.7E-07 | NTIIL1118998 | 421441 | 881827 | 6.86E+03 | 6.86E+03 |
| 4.7E-07 | NTIIL1119043 | 421416 | 881854 | 8.30E+03 | 8.30E+03 |
| 4.7E-07 | NTIIL1419397 | 415500 | 890315 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NTIIL167005A | 394758 | 893851 | 2.39E+04 | 2.39E+04 |
| 4.7E-07 | NTIIL18396 | 400823 | 873511 | 4.59E+04 | 4.59E+04 |
| 4.7E-07 | NTIIL1839883 | 400736 | 873843 | 2.32E+04 | 2.32E+04 |
| 4.7E-07 | NTIIL1839900 | 400739 | 873839 | 7.72E+03 | 6.42E+04 |
| 4.7E-07 | NTIIL227 | 422654 | 890333 | 1.49E+02 | 1.49E+02 |
| 4.7E-07 | NTIIL241 | 421200 | 890326 | 2.53E+04 | 2.53E+04 |
| 4.7E-07 | NTIIL292 | 421424 | 890426 | 1.64E+03 | 1.37E+04 |
| 4.7E-07 | NTIIN00247 | 413802 | 873039 | 1.16E+04 | 1.16E+04 |
| 4.7E-07 | NTIIN0390015 | 414132 | 855939 | 6.82E+04 | 6.82E+04 |
| 4.7E-07 | NTIKS00075 | 373904 | 972432 | 8.10E+04 | 8.10E+04 |
| 4.7E-07 | NTIKS00165 | 374002 | 972234 | 3.09E+04 | 3.09E+04 |
| 4.7E-07 | NTIKY1131 | 365812 | 862835 | 2.49E+05 | 2.49E+05 |
| 4.7E-07 | NTIKY1141 | 380328 | 844334 | 2.55E+03 | 2.55E+03 |
| 4.7E-07 | NTIKY1145 | 380354 | 844321 | 1.38E+02 | 1.15E+03 |
| 4.7E-07 | NTIKY719 | 380342 | 845540 | 5.65E+04 | 5.65E+04 |
| 4.7E-07 | NTIKY804 | 374602 | 870705 | 3.39E+03 | 3.39E+03 |
| 4.7E-07 | NTIKY829 | 380237 | 842813 | 2.32E+04 | 2.32E+04 |
| 4.7E-07 | NTIKY987 | 365108 | 865433 | 3.20E+04 | 3.20E+04 |
| 4.7E-07 | NTILA1150010 | 310255 | 931231 | 1.88E+01 | 3.39E+01 |
| 4.7E-07 | NTIMIA0155 | 423823 | 851901 | 2.49E+01 | 2.49E+01 |
| 4.7E-07 | NTIMIA2416 | 425310 | 853318 | 3.74E+03 | 3.74E+03 |
| 4.7E-07 | NTIMIA2447 | 425420 | 854038 | 1.53E+03 | 1.27E+04 |
| 4.7E-07 | NTIMIA2677 | 425559 | 854248 | 1.30E+04 | 1.30E+04 |
| 4.7E-07 | NTIMIA2931 | 423547 | 835615 | 3.06E+04 | 3.06E+04 |
| 4.7E-07 | NTIMIA4332 | 431228 | 861328 | 6.18E+03 | 6.18E+03 |
| 4.7E-07 | NTIMIB1904 | 431301 | 861541 | 3.51E+04 | 3.51E+04 |
| 4.7E-07 | NTIMIB2289 | 415335 | 840122 | 2.17E+04 | 2.17E+04 |
| 4.7E-07 | NTIMIB4096 | 415034 | 853947 | 3.31E+04 | 3.31E+04 |
| 4.7E-07 | NTIMIB4538 | 425526 | 854204 | 1.54E+02 | 1.54E+02 |
| 4.7E-07 | NTIMIB6220 | 423531 | 825153 | 1.81E+04 | 1.81E+04 |
| 4.7E-07 | NTIMIB7018 | 422852 | 832855 | 7.72E+03 | 7.72E+03 |
| 4.7E-07 | NTIMIM4403 | 421936 | 832507 | 2.69E+04 | 2.69E+04 |
| 4.7E-07 | NTIMIM4607 | 421125 | 831004 | 7.48E+03 | 7.48E+03 |
| 4.7E-07 | NTIMIN5540 | 420532 | 862511 | 1.51E+04 | 1.51E+04 |
| 4.7E-07 | NTIMIN5733 | 423139 | 830516 | 6.46E+03 | 6.46E+03 |
| 4.7E-07 | NTIMIN6173 | 451742 | 851510 | 2.08E+03 | 1.73E+04 |
| 4.7E-07 | NTIMIN6646 | 425947 | 841255 | 2.57E+03 | 2.57E+03 |
| 4.7E-07 | NTIMIN6660 | 423023 | 830704 | 1.29E+03 | 1.29E+03 |
| 4.7E-07 | NTIMN123294 | 445607 | 930433 | 1.26E+04 | 1.26E+04 |
| 4.7E-07 | NTIMN1429 | 441024 | 940245 | 4.17E+03 | 4.17E+03 |
| 4.7E-07 | NTIMN2713900 | 444706 | 933030 | 2.82E+03 | 2.82E+03 |
| 4.7E-07 | NTIMNT$8855 | 450500 | 932321 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NTIMNT$8860 | 450610 | 931558 | 3.19E+04 | 3.19E+04 |
| 4.7E-07 | NTIMS025298 | 333520 | 883859 | 1.37E+00 | 1.14E+01 |
| 4.7E-07 | NTIMS059302 | 303341 | 884902 | 7.49E+04 | 7.49E+04 |
| 4.7E-07 | NTINC787 | 353605 | 822208 | 6.91E+00 | 6.91E+00 |
| 4.7E-07 | NTINJNJ34410 | 403426 | 742429 | 1.70E+02 | 1.70E+02 |
| 4.7E-07 | NTINM0031 | 321617 | 1065713 | 1.89E+05 | 1.89E+05 |
| 4.7E-07 | NTINY013315 | 420533 | 791328 | 3.09E+04 | 3.09E+04 |
| 4.7E-07 | NTINY013316 | 420635 | 791223 | 2.89E+02 | 2.40E+03 |
| 4.7E-07 | NTINY2038 | 404553 | 731703 | 5.76E+04 | 5.76E+04 |
| 4.7E-07 | NTINY3333600 | 412404 | 735754 | 4.80E+00 | 3.99E+01 |
| 4.7E-07 | NTINY8265400 | 431333 | 772437 | 9.99E+02 | 9.99E+02 |
| 4.7E-07 | NTIOH0829700 | 394902 | 840213 | 3.43E+02 | 2.85E+03 |
| 4.7E-07 | NTIOH0857730 | 394856 | 841048 | 1.93E+04 | 1.93E+04 |
| 4.7E-07 | NTIOH0857770 | 394745 | 840802 | 4.05E+04 | 4.05E+04 |
| 4.7E-07 | NTIOHRR239 | 395753 | 833702 | 1.36E+03 | 1.36E+03 |
| 4.7E-07 | NTIOHRR255 | 394915 | 840024 | 1.16E+04 | 1.16E+04 |
| 4.7E-07 | NTIOHRR298 | 394754 | 835326 | 3.43E+02 | 2.85E+03 |
| 4.7E-07 | NTIOHRR299 | 394810 | 835419 | 7.21E+03 | 2.32E+04 |
| 4.7E-07 | NTIOHRR343 | 400223 | 841157 | 9.59E+03 | 7.97E+04 |
| 4.7E-07 | NTIOHRR364 | 395804 | 841155 | 9.65E+03 | 9.65E+03 |
| 4.7E-07 | NTIOHRR385 | 394654 | 841053 | 1.62E+04 | 1.62E+04 |
| 4.7E-07 | NTIOHRR386 | 394611 | 840857 | 2.06E+03 | 1.71E+04 |
| 4.7E-07 | NTIOHRR501 | 394500 | 841612 | 5.48E+03 | 4.56E+04 |
| 4.7E-07 | NTIOHRR524 | 394500 | 841612 | 3.32E+03 | 3.32E+03 |
| 4.7E-07 | NTIOHRR577 | 394727 | 841135 | 2.01E+04 | 2.01E+04 |
| 4.7E-07 | NTIOHT$6556 | 395426 | 841227 | 9.45E+03 | 2.95E+04 |
| 4.7E-07 | NTIOHT$6567 | 394547 | 841047 | 6.17E+03 | 5.12E+04 |
| 4.7E-07 | NTIOHT$6598 | 393912 | 841436 | 2.12E+04 | 2.12E+04 |
| 4.7E-07 | NTIOK1229 | 352819 | 980009 | 4.90E+03 | 4.90E+03 |
| 4.7E-07 | NTIOK2785 | 354341 | 952217 | 6.37E+03 | 6.37E+03 |
| 4.7E-07 | NTIOK4206 | 355706 | 955321 | 1.51E+04 | 1.51E+04 |
| 4.7E-07 | NTIOK4252 | 352839 | 974119 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NTIPA12304-3 | 415207 | 790901 | 4.63E+03 | 4.63E+03 |
| 4.7E-07 | NTIPA13304-3 | 395803 | 764517 | 2.35E+04 | 2.35E+04 |
| 4.7E-07 | NTIPA14-1682 | 401511 | 751647 | 9.65E+03 | 9.65E+03 |
| 4.7E-07 | NTIPA2098 | 402519 | 795319 | 3.14E+03 | 3.14E+03 |
| 4.7E-07 | NTIPA2187 | 410710 | 784540 | 1.43E+04 | 1.43E+04 |
| 4.7E-07 | NTIPA2244 | 400135 | 750154 | 4.63E+03 | 4.63E+03 |
| 4.7E-07 | NTIPA23-0419 | 400907 | 750048 | 1.39E+04 | 1.39E+04 |
| 4.7E-07 | NTIPA23-2947 | 400625 | 793503 | 1.30E+05 | 1.30E+05 |
| 4.7E-07 | NTIPA25-0932 | 414608 | 780501 | 1.16E+04 | 1.16E+04 |
| 4.7E-07 | NTIPA25-0946 | 410059 | 802500 | 5.87E+04 | 5.87E+04 |
| 4.7E-07 | NTIPA25-1054 | 401750 | 792330 | 1.93E+04 | 1.93E+04 |
| 4.7E-07 | NTIPA25-1355 | 414759 | 783800 | 6.18E+03 | 6.18E+03 |
| 4.7E-07 | NTIPA25-1645 | 405219 | 795022 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NTIPA48-1100 | 401308 | 751642 | 4.42E+04 | 4.42E+04 |
| 4.7E-07 | NTIRCA303707 | 372543 | 1220552 | 1.35E+03 | 1.35E+03 |
| 4.7E-07 | NTIRCA310521 | 373039 | 1221548 | 4.82E+03 | 4.82E+03 |
| 4.7E-07 | NTIRCA310581 | 374646 | 1221432 | 1.80E+02 | 1.80E+02 |
| 4.7E-07 | NTIRCA310599 | 374603 | 1221309 | 8.27E+02 | 8.27E+02 |
| 4.7E-07 | NTIRCA311021 | 372244 | 1215815 | 7.32E+00 | 7.32E+00 |
| 4.7E-07 | NTIRCA311226 | 380048 | 1220214 | 3.31E+03 | 3.31E+03 |
| 4.7E-07 | NTIRMN300066 | 450349 | 931606 | 4.88E+03 | 4.88E+03 |
| 4.7E-07 | NTIRMN301074 | 445718 | 931336 | 1.78E+04 | 1.78E+04 |
| 4.7E-07 | NTIRMN500041 | 445346 | 942248 | 8.98E+03 | 8.98E+03 |
| 4.7E-07 | NTIRSC0-0021 | 341223 | 820736 | 8.26E-01 | 6.87E+00 |
| 4.7E-07 | NTIRSC156063 | 335643 | 810716 | 3.63E+01 | 3.63E+01 |
| 4.7E-07 | NTISC2435 | 344039 | 821151 | 7.77E+03 | 7.77E+03 |
| 4.7E-07 | NTISCT$3360 | 340733 | 805213 | 8.28E+03 | 8.28E+03 |
| 4.7E-07 | NTIT$FNP1184 | 453416 | 1223556 | 3.78E+04 | 3.78E+04 |
| 4.7E-07 | NTITN0470 | 350111 | 851750 | 2.01E+03 | 2.01E+03 |
| 4.7E-07 | NTITXT$11375 | 325610 | 970556 | 3.09E+04 | 3.09E+04 |
| 4.7E-07 | NTITXT$11857 | 294912 | 981912 | 5.95E+04 | 5.95E+04 |
| 4.7E-07 | NTIVA6500005 | 370105 | 761927 | 1.51E+03 | 1.25E+04 |
| 4.7E-07 | NTIWA10203 | 474756 | 1223919 | 5.49E+03 | 5.49E+03 |
| 4.7E-07 | NTIWA13117 | 471656 | 1221418 | 1.59E+03 | 1.15E+04 |
| 4.7E-07 | NTIWA13120 | 475511 | 1221638 | 2.09E+05 | 2.09E+05 |
| 4.7E-07 | NTIWA14092 | 472421 | 1221454 | 9.45E+03 | 9.45E+03 |
| 4.7E-07 | NTIWA15119 | 475348 | 1221624 | 2.10E+02 | 2.10E+02 |
| 4.7E-07 | NTIWA16328 | 472346 | 1221400 | 2.40E+04 | 2.40E+04 |
| 4.7E-07 | NTIWA17771 | 470536 | 1222115 | 2.07E+02 | 1.26E+03 |
| 4.7E-07 | NTIWA28563 | 474020 | 1220539 | 8.98E+01 | 8.98E+01 |
| 4.7E-07 | NTIWI1280497 | 430454 | 885345 | 2.76E+02 | 2.76E+02 |
| 4.7E-07 | NTIWI1280585 | 430354 | 885518 | 2.51E+02 | 2.51E+02 |
| 4.7E-07 | NTIWI1541294 | 424623 | 891758 | 5.67E+03 | 5.67E+03 |
| 4.7E-07 | NTIWI2410141 | 430027 | 875826 | 4.34E+02 | 4.34E+02 |
| 4.7E-07 | NTIWI2410173 | 430855 | 880047 | 4.32E+02 | 4.32E+02 |
| 4.7E-07 | NTIWI2410342 | 430108 | 875447 | 1.76E+03 | 1.76E+03 |
| 4.7E-07 | NTIWI2410368 | 430256 | 875457 | 3.78E+03 | 3.78E+03 |
| 4.7E-07 | NTIWI2416654 | 425145 | 875915 | 1.16E+04 | 1.16E+04 |
| 4.7E-07 | NTIWI2419617 | 425202 | 875850 | 3.17E+04 | 3.17E+04 |
| 4.7E-07 | NTIWI2460526 | 432232 | 875258 | 8.88E+03 | 8.88E+03 |
| 4.7E-07 | NTIWI2520097 | 424452 | 874804 | 9.65E+03 | 9.65E+03 |
| 4.7E-07 | NTIWI2650061 | 424726 | 882322 | 2.08E+05 | 2.08E+05 |
| 4.7E-07 | NTIWI2680147 | 430509 | 881554 | 1.43E+04 | 1.43E+04 |
| 4.7E-07 | NTIWI2681860 | 430631 | 882903 | 7.39E+03 | 7.39E+03 |
| 4.7E-07 | NTIWI2682381 | 430252 | 881060 | 1.31E+04 | 1.31E+04 |
| 4.7E-07 | NTIWI4380172 | 450446 | 873836 | 1.24E+04 | 1.24E+04 |
| 4.7E-07 | NTIWI4711097 | 440949 | 882829 | 1.78E+04 | 1.78E+04 |
| 4.7E-07 | NTIWI6030598 | 453238 | 920103 | 1.08E+04 | 1.08E+04 |
| 4.7E-07 | NTIWI7440095 | 453755 | 892338 | 3.20E+04 | 3.20E+04 |

1 Fields omitted for this exhibit: Chemical name = MC equivalent; Facility ID Number (sequential; irrelevant as long as the numbering is consistent for each facility across all input files); Location (all halogenated solvent cleaning facilities are given a value of 1 for rural); Number of Emission Points (1 for all halogenated solvent cleaning facilities); Emission Point ID Number (1 for all halogenated solvent cleaning facilities); Vent Type (all halogenated solvent cleaning facilities are given a value of H for stack); Stack Height, Area, Vent Type, Diameter, Gas Exit Velocity, Gas Exit Temperature (see Exhibit C-1); Model Output Maps (all halogenated solvent cleaning facilities are given a value of ‘N – No’); Each Ring (all halogenated solvent cleaning facilities are given a value of ‘N – No’).
2 In HEM-SCREEN, latitude and longitude are presented as DDMMSS, where DD is degrees, MM is minutes, SS is seconds.  Longitude is in degrees West.

3 We evaluated risks separately using the California EPA (CalEPA) URE for perchloroethylene (PCE) of 5.9 × 10-6 (μg/m3)-1 and a URE for PCE developed by EPA’s Office of Prevention, Pesticides and Toxic Substance (OPPTS) of 7.1 × 10-7 (μg/m3)-1.

4 MC = methylene chloride.

Exhibit E-2

Selected Fields from the 2002 HEM-SCREEN Input for Carcinogen-Emitting Halogenated Solvent Cleaning Facilities1

| Unit Risk Factor (ug/m3)-1 | Facility Name | Latitude2 | Longitude2 | OPPTS3 MC4-Equivalent Emission Rate (kg/yr) | CalEPA3 MC4-Equivalent Emission Rate (kg/yr) |
| --- | --- | --- | --- | --- | --- |
| 4.7E-07 | NEI946 | 393849 | 1045959 | 1.70E+04 | 1.70E+04 |
| 4.7E-07 | NEI965 | 400344 | 1051223 | 2.25E+02 | 2.25E+02 |
| 4.7E-07 | NEI968 | 400859 | 1050646 | 9.76E+01 | 9.76E+01 |
| 4.7E-07 | NEI1367 | 394125 | 1045927 | 1.36E+02 | 1.36E+02 |
| 4.7E-07 | NEI1608 | 394508 | 1045236 | 7.99E+03 | 7.99E+03 |
| 4.7E-07 | NEI1830 | 384832 | 1044331 | 2.28E+03 | 1.89E+04 |
| 4.7E-07 | NEI2733 | 425254 | 711044 | 6.61E+04 | 6.61E+04 |
| 4.7E-07 | NEI3606 | 402527 | 1044154 | 3.42E+02 | 3.42E+02 |
| 4.7E-07 | NEI4694 | 400839 | 1050825 | 9.27E+01 | 9.27E+01 |
| 4.7E-07 | NEI4855 | 400514 | 1051055 | 2.38E+01 | 2.38E+01 |
| 4.7E-07 | NEI5372 | 404131 | 781344 | 9.23E+04 | 9.23E+04 |
| 4.7E-07 | NEI5410 | 400624 | 752036 | 5.24E+04 | 5.24E+04 |
| 4.7E-07 | NEI5994 | 300129 | 895501 | 3.96E+02 | 3.96E+02 |
| 4.7E-07 | NEI6135 | 295718 | 900902 | 5.32E+04 | 5.32E+04 |
| 4.7E-07 | NEI6225 | 413903 | 712830 | 7.72E+03 | 7.72E+03 |
| 4.7E-07 | NEI6360 | 413208 | 730157 | 5.25E+04 | 5.25E+04 |
| 4.7E-07 | NEI6536 | 324431 | 965847 | 4.86E+02 | 4.86E+02 |
| 4.7E-07 | NEI6596 | 321721 | 951513 | 5.00E+04 | 5.00E+04 |
| 4.7E-07 | NEI6865 | 322024 | 1023314 | 8.16E+02 | 8.16E+02 |
| 4.7E-07 | NEI6954 | 420404 | 790911 | 2.51E+04 | 2.51E+04 |
| 4.7E-07 | NEI7024 | 412517 | 783409 | 5.48E+04 | 5.48E+04 |
| 4.7E-07 | NEI7025 | 413320 | 783500 | 7.54E+03 | 7.54E+03 |
| 4.7E-07 | NEI7068 | 410100 | 802460 | 3.71E+04 | 3.71E+04 |
| 4.7E-07 | NEI7069 | 412120 | 802440 | 2.35E+05 | 2.35E+05 |
| 4.7E-07 | NEI7092 | 415239 | 800719 | 3.39E+04 | 2.82E+05 |
| 4.7E-07 | NEI7150 | 294014 | 964725 | 5.53E+03 | 5.53E+03 |
| 4.7E-07 | NEI7172 | 395405 | 763744 | 1.10E+05 | 1.10E+05 |
| 4.7E-07 | NEI7218 | 404810 | 762650 | 5.62E+03 | 4.67E+04 |
| 4.7E-07 | NEI7323 | 400606 | 750820 | 2.70E+03 | 2.70E+03 |
| 4.7E-07 | NEI7331 | 395611 | 751109 | 4.74E+04 | 4.74E+04 |
| 4.7E-07 | NEI7345 | 401001 | 752016 | 1.94E+05 | 1.94E+05 |
| 4.7E-07 | NEI7347 | 401139 | 752905 | 2.09E+05 | 2.09E+05 |
| 4.7E-07 | NEI7348 | 401112 | 752611 | 2.71E+05 | 2.71E+05 |
| 4.7E-07 | NEI7350 | 401528 | 751945 | 8.53E+03 | 8.53E+03 |
| 4.7E-07 | NEI7352 | 401309 | 751642 | 8.71E+03 | 8.71E+03 |
| 4.7E-07 | NEI7365 | 401916 | 760133 | 2.35E+04 | 2.35E+04 |
| 4.7E-07 | NEI7367 | 401923 | 755628 | 2.83E+05 | 2.83E+05 |
| 4.7E-07 | NEI7368 | 402132 | 755615 | 7.29E+03 | 7.29E+03 |
| 4.7E-07 | NEI7573 | 325329 | 964210 | 2.90E+03 | 2.90E+03 |
| 4.7E-07 | NEI7752 | 313957 | 943941 | 1.37E+02 | 1.14E+03 |
| 4.7E-07 | NEI7945 | 344758 | 822144 | 1.29E+04 | 1.29E+04 |
| 4.7E-07 | NEI7956 | 345740 | 822631 | 1.05E+04 | 8.70E+04 |
| 4.7E-07 | NEI8011 | 282509 | 964044 | 4.25E+01 | 4.25E+01 |
| 4.7E-07 | NEI8273 | 301336 | 814013 | 3.73E+03 | 3.73E+03 |
| 4.7E-07 | NEI8297 | 281840 | 804234 | 2.34E+04 | 2.34E+04 |
| 4.7E-07 | NEI8320 | 255537 | 801522 | 8.42E+04 | 8.42E+04 |
| 4.7E-07 | NEI8346 | 291931 | 810656 | 9.26E+04 | 9.26E+04 |
| 4.7E-07 | NEI8604 | 303257 | 880814 | 2.16E+04 | 2.16E+04 |
| 4.7E-07 | NEI10885 | 325019 | 965039 | 9.07E+00 | 9.07E+00 |
| 4.7E-07 | NEI11059 | 294342 | 950924 | 9.59E-01 | 7.97E+00 |
| 4.7E-07 | NEI11106 | 334930 | 894754 | 1.61E+05 | 1.61E+05 |
| 4.7E-07 | NEI11188 | 324256 | 970151 | 1.08E+03 | 1.08E+03 |
| 4.7E-07 | NEI11248 | 381235 | 851335 | 1.91E+04 | 1.91E+04 |
| 4.7E-07 | NEI11259 | 374638 | 845110 | 4.02E+04 | 4.02E+04 |
| 4.7E-07 | NEI11275 | 374141 | 841544 | 3.04E+01 | 3.04E+01 |
| 4.7E-07 | NEI11295 | 290154 | 952410 | 2.67E+01 | 2.22E+02 |
| 4.7E-07 | NEI11307 | 390150 | 842641 | 2.22E+04 | 2.22E+04 |
| 4.7E-07 | NEI11344 | 364410 | 863344 | 4.30E+04 | 4.30E+04 |
| 4.7E-07 | NEI11349 | 365232 | 873030 | 1.23E+04 | 1.23E+04 |
| 4.7E-07 | NEI11368 | 374140 | 875228 | 9.54E+04 | 9.54E+04 |
| 4.7E-07 | NEI11474 | 275301 | 971429 | 2.63E+03 | 2.63E+03 |
| 4.7E-07 | NEI11517 | 412860 | 814001 | 2.57E+04 | 2.57E+04 |
| 4.7E-07 | NEI11519 | 413449 | 813150 | 1.32E+05 | 1.32E+05 |
| 4.7E-07 | NEI11526 | 412358 | 812826 | 2.54E+03 | 2.11E+04 |
| 4.7E-07 | NEI11648 | 395329 | 834330 | 2.96E+05 | 2.96E+05 |
| 4.7E-07 | NEI11709 | 395415 | 861530 | 2.72E+02 | 2.72E+02 |
| 4.7E-07 | NEI11790 | 390733 | 855743 | 1.43E+04 | 1.43E+04 |
| 4.7E-07 | NEI11809 | 324953 | 971904 | 2.44E+04 | 2.44E+04 |
| 4.7E-07 | NEI11810 | 375846 | 873507 | 1.01E+03 | 1.01E+03 |
| 4.7E-07 | NEI11865 | 421933 | 835245 | 6.57E+03 | 6.57E+03 |
| 4.7E-07 | NEI11916 | 425923 | 841217 | 9.93E+03 | 9.93E+03 |
| 4.7E-07 | NEI11984 | 431252 | 861446 | 2.93E+04 | 2.93E+04 |
| 4.7E-07 | NEI11985 | 431358 | 861228 | 1.01E+04 | 1.01E+04 |
| 4.7E-07 | NEI11994 | 425642 | 854105 | 1.19E+05 | 1.19E+05 |
| 4.7E-07 | NEI12240 | 413229 | 902747 | 7.25E+04 | 6.03E+05 |
| 4.7E-07 | NEI12314 | 445657 | 931008 | 1.09E+04 | 1.09E+04 |
| 4.7E-07 | NEI12320 | 445248 | 931219 | 9.83E+04 | 9.83E+04 |
| 4.7E-07 | NEI12333 | 445131 | 933145 | 3.98E+03 | 3.98E+03 |
| 4.7E-07 | NEI12348 | 445659 | 931635 | 6.04E+04 | 6.04E+04 |
| 4.7E-07 | NEI12350 | 445857 | 931306 | 5.05E+04 | 5.05E+04 |
| 4.7E-07 | NEI12355 | 450000 | 932137 | 3.51E+04 | 3.51E+04 |
| 4.7E-07 | NEI12422 | 274151 | 971629 | 6.02E+02 | 6.02E+02 |
| 4.7E-07 | NEI12595 | 324622 | 970333 | 5.09E+04 | 4.19E+05 |
| 4.7E-07 | NEI12727 | 390456 | 944409 | 1.23E+04 | 1.23E+04 |
| 4.7E-07 | NEI12750 | 374454 | 971903 | 2.86E+02 | 2.86E+02 |
| 4.7E-07 | NEI12927 | 352811 | 974246 | 7.26E+01 | 7.26E+01 |
| 4.7E-07 | NEI12930 | 352518 | 972331 | 1.67E+04 | 9.73E+04 |
| 4.7E-07 | NEI12973 | 361041 | 955115 | 1.36E+04 | 1.36E+04 |
| 4.7E-07 | NEI12974 | 362225 | 954947 | 1.63E+03 | 1.36E+04 |
| 4.7E-07 | NEI13038 | 324857 | 965610 | 4.39E+00 | 3.64E+01 |
| 4.7E-07 | NEI13146 | 393904 | 1050144 | 8.69E+03 | 8.69E+03 |
| 4.7E-07 | NEI13238 | 294207 | 952352 | 2.74E-01 | 2.28E+00 |
| 4.7E-07 | NEI13309 | 324618 | 963914 | 7.61E+02 | 7.61E+02 |
| 4.7E-07 | NEI13336 | 453243 | 1222803 | 8.05E+03 | 5.81E+04 |
| 4.7E-07 | NEI18329 | 333815 | 855511 | 1.91E+05 | 1.91E+05 |
| 4.7E-07 | NEI18760 | 374427 | 1221222 | 2.59E+01 | 2.59E+01 |
| 4.7E-07 | NEI18906 | 374048 | 1214553 | 6.46E+01 | 5.37E+02 |
| 4.7E-07 | NEI18907 | 374236 | 1215537 | 3.01E+03 | 3.01E+03 |
| 4.7E-07 | NEI19032 | 373836 | 1220747 | 1.55E+04 | 1.55E+04 |
| 4.7E-07 | NEI19053 | 374627 | 1221457 | 8.82E+02 | 8.82E+02 |
| 4.7E-07 | NEI19090 | 375159 | 1221756 | 1.17E+01 | 1.17E+01 |
| 4.7E-07 | NEI19091 | 374143 | 1214231 | 2.62E+01 | 2.62E+01 |
| 4.7E-07 | NEI19927 | 363031 | 1193257 | 7.75E+01 | 7.75E+01 |
| 4.7E-07 | NEI19932 | 364904 | 1195416 | 4.34E+03 | 4.34E+03 |
| 4.7E-07 | NEI20237 | 340758 | 1181551 | 1.53E+03 | 1.27E+04 |
| 4.7E-07 | NEI20243 | 340607 | 1181438 | 1.93E+03 | 1.93E+03 |
| 4.7E-07 | NEI20246 | 335554 | 1180717 | 2.24E+03 | 2.24E+03 |
| 4.7E-07 | NEI20256 | 341348 | 1182140 | 3.70E+03 | 3.07E+04 |
| 4.7E-07 | NEI20272 | 335309 | 1180104 | 1.15E+04 | 9.58E+04 |
| 4.7E-07 | NEI20273 | 335625 | 1182514 | 2.69E+03 | 2.69E+03 |
| 4.7E-07 | NEI20276 | 341612 | 1182552 | 1.67E+03 | 1.39E+04 |
| 4.7E-07 | NEI20284 | 335043 | 1182028 | 7.05E+00 | 7.05E+00 |
| 4.7E-07 | NEI20317 | 340412 | 1181016 | 8.71E+03 | 7.24E+04 |
| 4.7E-07 | NEI20336 | 341019 | 1181853 | 6.12E+00 | 5.08E+01 |
| 4.7E-07 | NEI20337 | 341335 | 1182224 | 7.60E+02 | 7.60E+02 |
| 4.7E-07 | NEI20353 | 340148 | 1182552 | 1.20E+02 | 1.20E+02 |
| 4.7E-07 | NEI20357 | 340513 | 1180304 | 1.29E+02 | 1.29E+02 |
| 4.7E-07 | NEI20372 | 341124 | 1182252 | 1.72E+02 | 1.11E+03 |
| 4.7E-07 | NEI20390 | 335600 | 1180420 | 3.77E+02 | 3.13E+03 |
| 4.7E-07 | NEI20411 | 340336 | 1180940 | 4.63E+02 | 4.63E+02 |
| 4.7E-07 | NEI20415 | 340224 | 1174728 | 5.48E+02 | 5.48E+02 |
| 4.7E-07 | NEI20508 | 340448 | 1181952 | 8.00E+03 | 6.65E+04 |
| 4.7E-07 | NEI20511 | 335624 | 1182516 | 1.29E+04 | 1.29E+04 |
| 4.7E-07 | NEI20517 | 335248 | 1181540 | 5.52E+03 | 4.59E+04 |
| 4.7E-07 | NEI20538 | 341433 | 1183538 | 5.00E+02 | 4.15E+03 |
| 4.7E-07 | NEI20553 | 335949 | 1175445 | 2.17E+02 | 2.17E+02 |
| 4.7E-07 | NEI20571 | 335454 | 1181835 | 2.35E+03 | 2.35E+03 |
| 4.7E-07 | NEI20588 | 335360 | 1181652 | 1.65E+03 | 1.37E+04 |
| 4.7E-07 | NEI20600 | 335345 | 1180244 | 8.27E+02 | 8.27E+02 |
| 4.7E-07 | NEI20606 | 335053 | 1181348 | 1.49E+04 | 1.24E+05 |
| 4.7E-07 | NEI20615 | 335360 | 1182252 | 2.62E+02 | 2.62E+02 |
| 4.7E-07 | NEI20617 | 340546 | 1180147 | 8.44E+02 | 4.88E+03 |
| 4.7E-07 | NEI20618 | 340824 | 1181616 | 2.37E+03 | 1.66E+04 |
| 4.7E-07 | NEI20675 | 340712 | 1181504 | 4.49E+01 | 4.49E+01 |
| 4.7E-07 | NEI20698 | 340535 | 1174311 | 3.02E+03 | 3.02E+03 |
| 4.7E-07 | NEI20749 | 334836 | 1180828 | 3.75E+02 | 3.75E+02 |
| 4.7E-07 | NEI20758 | 340260 | 1174804 | 1.31E+04 | 1.31E+04 |
| 4.7E-07 | NEI20787 | 335457 | 1182324 | 3.21E+01 | 3.21E+01 |
| 4.7E-07 | NEI20827 | 335510 | 1182359 | 2.33E+03 | 1.94E+04 |
| 4.7E-07 | NEI20860 | 340001 | 1180422 | 1.34E+03 | 1.34E+03 |
| 4.7E-07 | NEI20861 | 335436 | 1180304 | 4.31E+03 | 4.31E+03 |
| 4.7E-07 | NEI20890 | 335528 | 1182552 | 9.53E+00 | 9.53E+00 |
| 4.7E-07 | NEI20904 | 340218 | 1181421 | 3.22E+01 | 3.22E+01 |
| 4.7E-07 | NEI20926 | 334629 | 1181536 | 2.90E+01 | 3.21E+01 |
| 4.7E-07 | NEI20940 | 340057 | 1175014 | 3.43E+01 | 3.43E+01 |
| 4.7E-07 | NEI20942 | 335237 | 1181345 | 2.50E+03 | 2.50E+03 |
| 4.7E-07 | NEI20950 | 335324 | 1181016 | 7.71E+03 | 6.40E+04 |
| 4.7E-07 | NEI20955 | 334648 | 1180940 | 1.94E+01 | 1.94E+01 |
| 4.7E-07 | NEI20982 | 335020 | 1182012 | 4.76E+02 | 3.95E+03 |
| 4.7E-07 | NEI21018 | 335660 | 1180904 | 2.42E+03 | 2.01E+04 |
| 4.7E-07 | NEI21019 | 340803 | 1180011 | 4.94E+02 | 4.11E+03 |
| 4.7E-07 | NEI21020 | 334633 | 1181513 | 7.42E+01 | 6.16E+02 |
| 4.7E-07 | NEI21058 | 335024 | 1181355 | 9.98E+00 | 9.98E+00 |
| 4.7E-07 | NEI21068 | 340448 | 1180228 | 3.82E+03 | 3.82E+03 |
| 4.7E-07 | NEI21071 | 341536 | 1183433 | 3.55E+01 | 3.55E+01 |
| 4.7E-07 | NEI21090 | 341424 | 1182328 | 5.44E+02 | 5.44E+02 |
| 4.7E-07 | NEI21108 | 335446 | 1181824 | 3.12E-01 | 2.59E+00 |
| 4.7E-07 | NEI21153 | 340748 | 1175516 | 9.25E+01 | 7.69E+02 |
| 4.7E-07 | NEI21168 | 335956 | 1175355 | 7.77E+02 | 6.46E+03 |
| 4.7E-07 | NEI21181 | 335324 | 1180228 | 1.39E+02 | 1.16E+03 |
| 4.7E-07 | NEI21226 | 341212 | 1182443 | 7.59E+02 | 7.59E+02 |
| 4.7E-07 | NEI21235 | 340260 | 1175928 | 3.00E+02 | 3.00E+02 |
| 4.7E-07 | NEI21236 | 335947 | 1181710 | 3.86E+02 | 1.44E+03 |
| 4.7E-07 | NEI21249 | 340100 | 1180230 | 1.63E+01 | 1.35E+02 |
| 4.7E-07 | NEI21255 | 340759 | 1175510 | 2.65E+03 | 2.20E+04 |
| 4.7E-07 | NEI21267 | 335248 | 1181652 | 1.05E+03 | 8.72E+03 |
| 4.7E-07 | NEI21281 | 340134 | 1182224 | 1.83E+02 | 1.52E+03 |
| 4.7E-07 | NEI21282 | 341206 | 1182033 | 8.46E+03 | 7.03E+04 |
| 4.7E-07 | NEI21339 | 335827 | 1181456 | 3.05E+04 | 2.53E+05 |
| 4.7E-07 | NEI21349 | 335960 | 1180716 | 5.50E+02 | 2.78E+03 |
| 4.7E-07 | NEI21350 | 335360 | 1181804 | 1.24E+03 | 4.80E+03 |
| 4.7E-07 | NEI21365 | 340112 | 1175816 | 8.86E+03 | 7.36E+04 |
| 4.7E-07 | NEI21378 | 340824 | 1182140 | 1.31E+04 | 1.09E+05 |
| 4.7E-07 | NEI21407 | 340112 | 1182740 | 3.16E+03 | 2.62E+04 |
| 4.7E-07 | NEI21436 | 335039 | 1182040 | 6.80E+01 | 3.59E+02 |
| 4.7E-07 | NEI21439 | 335624 | 1182440 | 1.81E+00 | 1.81E+00 |
| 4.7E-07 | NEI21445 | 335920 | 1181249 | 1.64E+03 | 1.64E+03 |
| 4.7E-07 | NEI21450 | 340636 | 1181428 | 1.34E+03 | 1.11E+04 |
| 4.7E-07 | NEI21452 | 335248 | 1182216 | 8.87E+02 | 8.87E+02 |
| 4.7E-07 | NEI21463 | 340048 | 1175454 | 1.85E-01 | 1.54E+00 |
| 4.7E-07 | NEI21478 | 341212 | 1182344 | 4.70E+02 | 4.70E+02 |
| 4.7E-07 | NEI21499 | 334455 | 1181443 | 1.22E+02 | 1.01E+03 |
| 4.7E-07 | NEI21516 | 334760 | 1181728 | 3.85E+03 | 3.85E+03 |
| 4.7E-07 | NEI21544 | 341634 | 1182546 | 4.01E+02 | 4.01E+02 |
| 4.7E-07 | NEI21573 | 340013 | 1180744 | 4.84E+01 | 4.02E+02 |
| 4.7E-07 | NEI21961 | 335136 | 1175328 | 2.46E+03 | 2.04E+04 |
| 4.7E-07 | NEI21991 | 334638 | 1180004 | 1.68E+04 | 1.40E+05 |
| 4.7E-07 | NEI22010 | 335241 | 1175323 | 2.24E-01 | 1.86E+00 |
| 4.7E-07 | NEI22045 | 334760 | 1175140 | 8.22E+00 | 6.83E+01 |
| 4.7E-07 | NEI22048 | 333803 | 1175609 | 2.54E+01 | 2.54E+01 |
| 4.7E-07 | NEI22066 | 334246 | 1175509 | 8.91E-01 | 7.40E+00 |
| 4.7E-07 | NEI22067 | 334432 | 1175813 | 1.03E+03 | 8.60E+03 |
| 4.7E-07 | NEI22117 | 335136 | 1175328 | 6.40E+02 | 6.40E+02 |
| 4.7E-07 | NEI22124 | 335045 | 1175955 | 6.74E+00 | 5.60E+01 |
| 4.7E-07 | NEI22137 | 335132 | 1174830 | 6.42E+02 | 6.42E+02 |
| 4.7E-07 | NEI22153 | 334440 | 1180212 | 2.77E+03 | 3.01E+03 |
| 4.7E-07 | NEI22160 | 335146 | 1175315 | 9.68E+04 | 8.05E+05 |
| 4.7E-07 | NEI22162 | 334236 | 1175404 | 1.30E+04 | 1.08E+05 |
| 4.7E-07 | NEI22176 | 334230 | 1175556 | 7.62E+03 | 7.62E+03 |
| 4.7E-07 | NEI22192 | 334015 | 1175051 | 3.41E+04 | 2.84E+05 |
| 4.7E-07 | NEI22207 | 334144 | 1174954 | 2.51E+01 | 2.51E+01 |
| 4.7E-07 | NEI22254 | 335140 | 1175149 | 2.75E+02 | 2.75E+02 |
| 4.7E-07 | NEI22255 | 334130 | 1175104 | 2.83E+02 | 2.83E+02 |
| 4.7E-07 | NEI22259 | 334312 | 1175104 | 3.24E+02 | 2.69E+03 |
| 4.7E-07 | NEI22260 | 334246 | 1175509 | 4.81E+02 | 4.81E+02 |
| 4.7E-07 | NEI22295 | 334348 | 1180152 | 3.36E+03 | 2.79E+04 |
| 4.7E-07 | NEI22323 | 334724 | 1175216 | 1.93E+01 | 5.44E+01 |
| 4.7E-07 | NEI22326 | 334760 | 1180304 | 8.67E+03 | 7.21E+04 |
| 4.7E-07 | NEI22372 | 333950 | 1161245 | 1.35E+03 | 1.35E+03 |
| 4.7E-07 | NEI22375 | 335157 | 1171530 | 1.36E+00 | 1.13E+01 |
| 4.7E-07 | NEI22474 | 335324 | 1171428 | 7.37E+02 | 7.37E+02 |
| 4.7E-07 | NEI22485 | 383755 | 1211231 | 6.89E+01 | 9.73E+01 |
| 4.7E-07 | NEI22652 | 383541 | 1212928 | 8.00E+02 | 6.65E+03 |
| 4.7E-07 | NEI22679 | 382946 | 1212719 | 3.71E+01 | 3.71E+01 |
| 4.7E-07 | NEI22744 | 340432 | 1173004 | 2.08E+03 | 2.08E+03 |
| 4.7E-07 | NEI22848 | 353926 | 1173944 | 1.22E+02 | 1.22E+02 |
| 4.7E-07 | NEI22907 | 340329 | 1174116 | 4.49E+01 | 4.49E+01 |
| 4.7E-07 | NEI22941 | 345342 | 1165155 | 4.62E+00 | 3.74E+01 |
| 4.7E-07 | NEI22952 | 340533 | 1173810 | 5.76E+04 | 4.78E+05 |
| 4.7E-07 | NEI23077 | 324122 | 1170804 | 4.01E+00 | 3.33E+01 |
| 4.7E-07 | NEI23188 | 331454 | 1172357 | 2.34E+01 | 1.46E+02 |
| 4.7E-07 | NEI23510 | 374500 | 1222606 | 5.10E+02 | 4.24E+03 |
| 4.7E-07 | NEI24080 | 373403 | 1221843 | 2.42E+03 | 2.42E+03 |
| 4.7E-07 | NEI24755 | 372145 | 1215701 | 5.12E+02 | 4.26E+03 |
| 4.7E-07 | NEI24823 | 371208 | 1214942 | 4.01E+01 | 4.01E+01 |
| 4.7E-07 | NEI24980 | 372321 | 1220602 | 5.02E-01 | 5.02E-01 |
| 4.7E-07 | NEI25016 | 371633 | 1215636 | 5.18E+03 | 5.18E+03 |
| 4.7E-07 | NEI25038 | 372444 | 1215314 | 1.29E+03 | 1.29E+03 |
| 4.7E-07 | NEI25245 | 372237 | 1220142 | 1.50E+02 | 1.50E+02 |
| 4.7E-07 | NEI25264 | 371402 | 1214429 | 2.52E+01 | 2.52E+01 |
| 4.7E-07 | NEI25515 | 381449 | 1215701 | 4.11E+01 | 4.11E+01 |
| 4.7E-07 | NEI25756 | 382552 | 1224253 | 5.53E+01 | 5.53E+01 |
| 4.7E-07 | NEI25896 | 374358 | 1205611 | 4.51E+02 | 3.28E+03 |
| 4.7E-07 | NEI25970 | 341131 | 1185511 | 7.40E+01 | 6.15E+02 |
| 4.7E-07 | NEI25972 | 340948 | 1191318 | 1.76E+00 | 1.41E+01 |
| 4.7E-07 | NEI25980 | 341503 | 1191338 | 5.44E+02 | 5.44E+02 |
| 4.7E-07 | NEI25984 | 340850 | 1191017 | 6.32E+01 | 6.32E+01 |
| 4.7E-07 | NEI26014 | 340842 | 1191119 | 2.25E+01 | 2.25E+01 |
| 4.7E-07 | NEI26022 | 341722 | 1185128 | 1.05E+03 | 1.05E+03 |
| 4.7E-07 | NEI26038 | 341612 | 1184223 | 2.49E+01 | 2.49E+01 |
| 4.7E-07 | NEI26056 | 341225 | 1190742 | 4.02E+01 | 4.02E+01 |
| 4.7E-07 | NEI26059 | 341531 | 1191437 | 6.37E+02 | 5.29E+03 |
| 4.7E-07 | NEI26060 | 341452 | 1184031 | 1.46E+04 | 1.46E+04 |
| 4.7E-07 | NEI26095 | 341317 | 1190917 | 5.34E+00 | 4.44E+01 |
| 4.7E-07 | NEI26104 | 340942 | 1191313 | 2.86E+00 | 2.38E+01 |
| 4.7E-07 | NEI26183 | 390635 | 753319 | 2.46E+04 | 2.46E+04 |
| 4.7E-07 | NEI31242 | 410513 | 851419 | 2.99E+05 | 2.99E+05 |
| 4.7E-07 | NEI31360 | 390201 | 845804 | 3.06E+04 | 3.06E+04 |
| 4.7E-07 | NEI31387 | 412518 | 845146 | 6.53E+03 | 6.53E+03 |
| 4.7E-07 | NEI31662 | 394130 | 850832 | 3.72E+03 | 3.72E+03 |
| 4.7E-07 | NEI31774 | 402726 | 860626 | 2.12E+04 | 2.12E+04 |
| 4.7E-07 | NEI31789 | 405157 | 853122 | 1.06E+04 | 1.06E+04 |
| 4.7E-07 | NEI32072 | 394401 | 861240 | 8.49E+03 | 7.05E+04 |
| 4.7E-07 | NEI32265 | 400224 | 865248 | 5.44E+04 | 5.44E+04 |
| 4.7E-07 | NEI32399 | 412754 | 862945 | 2.04E+03 | 2.04E+03 |
| 4.7E-07 | NEI32428 | 413924 | 860960 | 7.82E+03 | 7.82E+03 |
| 4.7E-07 | NEI32786 | 390125 | 944252 | 2.31E+04 | 1.92E+05 |
| 4.7E-07 | NEI32801 | 382051 | 974009 | 4.62E+01 | 3.84E+02 |
| 4.7E-07 | NEI32829 | 373950 | 972302 | 3.06E+04 | 3.06E+04 |
| 4.7E-07 | NEI32831 | 373727 | 971650 | 3.32E+05 | 5.40E+05 |
| 4.7E-07 | NEI32870 | 374052 | 855510 | 2.04E+04 | 2.04E+04 |
| 4.7E-07 | NEI33721 | 382344 | 753527 | 1.48E+05 | 1.48E+05 |
| 4.7E-07 | NEI34245 | 383307 | 910029 | 1.52E+04 | 1.52E+04 |
| 4.7E-07 | NEI34246 | 383409 | 910339 | 1.74E+04 | 1.74E+04 |
| 4.7E-07 | NEI34261 | 371121 | 931940 | 1.81E+01 | 1.81E+01 |
| 4.7E-07 | NEI34377 | 385732 | 943436 | 3.31E+01 | 2.75E+02 |
| 4.7E-07 | NEI34386 | 370540 | 943140 | 3.89E+03 | 3.89E+03 |
| 4.7E-07 | NEI34395 | 370346 | 942810 | 3.93E+02 | 3.93E+02 |
| 4.7E-07 | NEI34460 | 385836 | 913028 | 1.89E+04 | 1.89E+04 |
| 4.7E-07 | NEI34493 | 384240 | 931139 | 1.61E+05 | 1.61E+05 |
| 4.7E-07 | NEI34514 | 391751 | 944137 | 3.18E+03 | 2.64E+04 |
| 4.7E-07 | NEI34540 | 384841 | 902824 | 9.20E+03 | 9.20E+03 |
| 4.7E-07 | NEI34632 | 384535 | 902147 | 2.34E+04 | 2.34E+04 |
| 4.7E-07 | NEI34658 | 383538 | 902954 | 3.10E+05 | 3.10E+05 |
| 4.7E-07 | NEI34673 | 383647 | 901955 | 6.29E+03 | 5.23E+04 |
| 4.7E-07 | NEI34682 | 384406 | 902101 | 3.14E+01 | 2.52E+02 |
| 4.7E-07 | NEI34730 | 383712 | 901650 | 1.62E+04 | 1.62E+04 |
| 4.7E-07 | NEI34784 | 383423 | 901402 | 1.49E+02 | 1.24E+03 |
| 4.7E-07 | NEI35612 | 421760 | 752324 | 1.20E+05 | 1.20E+05 |
| 4.7E-07 | NEI36095 | 403936 | 735400 | 2.99E+04 | 2.99E+04 |
| 4.7E-07 | NEI36181 | 404330 | 740000 | 1.66E+04 | 1.66E+04 |
| 4.7E-07 | NEI37022 | 431200 | 773824 | 9.21E+01 | 9.21E+01 |
| 4.7E-07 | NEI38155 | 430505 | 751515 | 8.93E+03 | 8.93E+03 |
| 4.7E-07 | NEI39761 | 404200 | 732212 | 9.30E+03 | 7.73E+04 |
| 4.7E-07 | NEI40416 | 412437 | 814704 | 6.69E+02 | 5.56E+03 |
| 4.7E-07 | NEI41241 | 325048 | 800020 | 1.85E+03 | 1.85E+03 |
| 4.7E-07 | NEI41252 | 325324 | 795812 | 6.45E-01 | 5.36E+00 |
| 4.7E-07 | NEI41338 | 344114 | 821358 | 1.45E+03 | 1.45E+03 |
| 4.7E-07 | NEI42005 | 414000 | 1122560 | 4.84E+03 | 4.84E+03 |
| 4.7E-07 | NEI42018 | 410701 | 1115837 | 4.36E+02 | 2.67E+03 |
| 4.7E-07 | NEI42400 | 474520 | 1172313 | 6.41E+03 | 6.41E+03 |
| 4.7E-07 | NEI42671 | 440449 | 874210 | 5.64E+04 | 5.64E+04 |
| 4.7E-07 | NEI42701 | 445338 | 875344 | 1.19E+04 | 1.19E+04 |
| 4.7E-07 | NEI42711 | 431905 | 875733 | 9.10E+03 | 9.10E+03 |
| 4.7E-07 | NEI42750 | 424337 | 874726 | 6.01E+03 | 6.01E+03 |
| 4.7E-07 | NEI43004 | 433755 | 884405 | 1.43E+04 | 1.43E+04 |
| 4.7E-07 | NEI43378 | 360713 | 864136 | 2.77E+04 | 2.77E+04 |
| 4.7E-07 | NEI44511 | 451249 | 932441 | 5.05E+03 | 5.05E+03 |
| 4.7E-07 | NEI44674 | 360450 | 791450 | 1.80E+04 | 1.49E+05 |
| 4.7E-07 | NEI44730 | 445454 | 932456 | 3.82E+03 | 3.82E+03 |
| 4.7E-07 | NEI45064 | 350936 | 790017 | 6.40E+00 | 6.40E+00 |
| 4.7E-07 | NEI45127 | 414700 | 713103 | 4.35E+03 | 4.35E+03 |
| 4.7E-07 | NEI45203 | 345522 | 765322 | 9.27E+01 | 1.59E+02 |
| 4.7E-07 | NEI45208 | 345337 | 765348 | 8.94E+03 | 8.94E+03 |
| 4.7E-07 | NEI45456 | 445921 | 931525 | 3.83E+03 | 3.83E+03 |
| 4.7E-07 | NEI45529 | 414903 | 712640 | 1.65E+02 | 1.65E+02 |
| 4.7E-07 | NEI45542 | 414728 | 712403 | 2.95E+03 | 2.95E+03 |
| 4.7E-07 | NEI46603 | 473313 | 1221947 | 3.02E+04 | 3.02E+04 |
| 4.7E-07 | NEI47624 | 414550 | 874454 | 3.06E+04 | 3.06E+04 |
| 4.7E-07 | NEI48022 | 415624 | 875237 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NEI48035 | 415617 | 875302 | 2.99E+04 | 2.99E+04 |
| 4.7E-07 | NEI48062 | 415707 | 875321 | 1.78E+04 | 1.78E+04 |
| 4.7E-07 | NEI48274 | 420106 | 874719 | 7.64E+03 | 7.64E+03 |
| 4.7E-07 | NEI48296 | 420204 | 875346 | 1.15E+04 | 1.15E+04 |
| 4.7E-07 | NEI48353 | 420556 | 880217 | 9.43E+04 | 9.43E+04 |
| 4.7E-07 | NEI48419 | 420119 | 875750 | 7.13E+03 | 5.92E+04 |
| 4.7E-07 | NEI48445 | 415757 | 875222 | 3.63E+04 | 3.63E+04 |
| 4.7E-07 | NEI48447 | 415802 | 875158 | 3.07E+04 | 3.07E+04 |
| 4.7E-07 | NEI48568 | 420747 | 875523 | 7.89E+03 | 7.89E+03 |
| 4.7E-07 | NEI48613 | 415922 | 881042 | 2.57E+05 | 2.57E+05 |
| 4.7E-07 | NEI48676 | 420014 | 875752 | 2.64E+04 | 2.64E+04 |
| 4.7E-07 | NEI48889 | 415626 | 874135 | 5.44E+03 | 5.44E+03 |
| 4.7E-07 | NEI48914 | 415457 | 874451 | 8.43E+03 | 8.43E+03 |
| 4.7E-07 | NEI49391 | 415700 | 873946 | 1.45E+04 | 1.45E+04 |
| 4.7E-07 | NEI49427 | 415307 | 873927 | 5.27E+04 | 5.27E+04 |
| 4.7E-07 | NEI49525 | 415544 | 874354 | 1.71E+04 | 1.71E+04 |
| 4.7E-07 | NEI49526 | 414820 | 874232 | 1.75E+04 | 1.75E+04 |
| 4.7E-07 | NEI49625 | 415114 | 874411 | 8.89E+04 | 8.89E+04 |
| 4.7E-07 | NEI50167 | 414420 | 875615 | 1.72E+04 | 1.72E+04 |
| 4.7E-07 | NEI51064 | 414018 | 883215 | 4.82E+03 | 4.82E+03 |
| 4.7E-07 | NEI51726 | 421441 | 881912 | 1.04E+04 | 1.04E+04 |
| 4.7E-07 | NEI51753 | 421030 | 882543 | 1.26E+03 | 1.26E+03 |
| 4.7E-07 | NEI52191 | 384109 | 900959 | 2.18E+03 | 2.18E+03 |
| 4.7E-07 | NEI52497 | 420746 | 891525 | 3.06E+05 | 3.06E+05 |
| 4.7E-07 | NEI53014 | 383531 | 901021 | 1.77E+05 | 1.77E+05 |
| 4.7E-07 | NEI53153 | 395100 | 891643 | 1.69E+01 | 1.69E+01 |
| 4.7E-07 | NEI53352 | 400831 | 873649 | 1.20E+02 | 9.98E+02 |
| 4.7E-07 | NEI53562 | 413739 | 895714 | 1.31E+04 | 1.31E+04 |
| 4.7E-07 | NEI53688 | 412654 | 874504 | 3.36E+04 | 3.36E+04 |
| 4.7E-07 | NEI54141 | 360659 | 864428 | 5.67E-01 | 4.71E+00 |
| 4.7E-07 | NEI54795 | 415657 | 875207 | 1.10E+04 | 1.10E+04 |
| 4.7E-07 | NEI54855 | 420116 | 875744 | 1.53E+04 | 1.53E+04 |
| 4.7E-07 | NEI54885 | 415850 | 874546 | 1.41E+04 | 1.41E+04 |
| 4.7E-07 | NEI54963 | 415508 | 873947 | 1.97E+04 | 1.97E+04 |
| 4.7E-07 | NEI55239 | 414806 | 880345 | 7.22E+04 | 7.22E+04 |
| 4.7E-07 | NEI55719 | 422618 | 881459 | 3.61E+04 | 3.61E+04 |
| 4.7E-07 | NEI55774 | 394914 | 885755 | 7.93E+03 | 7.93E+03 |
| 4.7E-07 | NEI56886 | 431112 | 851415 | 5.53E+02 | 5.53E+02 |
| 4.7E-07 | NEI2CA124904 | 340140 | 1181411 | 3.79E+01 | 3.15E+02 |
| 4.7E-07 | NEI2CA130344 | 335420 | 1181627 | 8.16E+03 | 5.57E+04 |
| 4.7E-07 | NEI2CA133660 | 335248 | 1173524 | 4.28E+00 | 8.21E+00 |
| 4.7E-07 | NEI2CA251063 | 342554 | 1195427 | 8.22E+00 | 6.83E+01 |
| 4.7E-07 | NEI2CA271567 | 330437 | 1163560 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NEI2CA272317 | 324714 | 1165839 | 2.04E+03 | 1.69E+04 |
| 4.7E-07 | NEI2CA274026 | 324310 | 1171330 | 6.69E+01 | 6.69E+01 |
| 4.7E-07 | NEI2CA275448 | 324237 | 1171330 | 1.25E+02 | 1.25E+02 |
| 4.7E-07 | NEI2CA512150 | 345655 | 1175317 | 1.95E+00 | 1.62E+01 |
| 4.7E-07 | NEI2CA789244 | 324524 | 1171312 | 2.10E+03 | 2.10E+03 |
| 4.7E-07 | NEI2CA791411 | 330812 | 1171318 | 1.05E+00 | 6.53E+00 |
| 4.7E-07 | NEI2CA798094 | 324904 | 1165744 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NEI2CA798332 | 330852 | 1171359 | 3.40E+01 | 3.40E+01 |
| 4.7E-07 | NEI2CO123356 | 400458 | 1045904 | 8.88E+03 | 8.88E+03 |
| 4.7E-07 | NEI2CO1235 | 395903 | 1050524 | 5.64E+02 | 5.64E+02 |
| 4.7E-07 | NEI2CO1238 | 400204 | 1051360 | 2.85E+03 | 2.85E+03 |
| 4.7E-07 | NEI2IL005AMV | 415559 | 880231 | 2.19E+04 | 2.19E+04 |
| 4.7E-07 | NEI2IL015APF | 395056 | 885912 | 2.07E+04 | 2.07E+04 |
| 4.7E-07 | NEI2IL045AAP | 420416 | 882953 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NEI2IL060AAX | 414746 | 882024 | 1.58E+04 | 1.58E+04 |
| 4.7E-07 | NEI2IL096ANM | 415631 | 875411 | 1.32E+04 | 1.32E+04 |
| 4.7E-07 | NEI2IL153ACB | 414910 | 875147 | 4.94E+03 | 4.94E+03 |
| 4.7E-07 | NEI2IL186AHK | 415345 | 875200 | 4.17E+03 | 4.17E+03 |
| 4.7E-07 | NEI2IL186AHR | 415402 | 875150 | 9.64E+03 | 9.64E+03 |
| 4.7E-07 | NEI2IL195AAA | 414616 | 894345 | 1.01E+05 | 8.42E+05 |
| 4.7E-07 | NEI2IL306AAP | 420105 | 880849 | 9.56E+03 | 9.56E+03 |
| 4.7E-07 | NEI2IL440AMC | 415943 | 875749 | 2.24E+03 | 2.24E+03 |
| 4.7E-07 | NEI2IL489AAP | 420004 | 880611 | 5.08E+03 | 5.08E+03 |
| 4.7E-07 | NEI2IN097373 | 394454 | 861530 | 1.07E+04 | 1.07E+04 |
| 4.7E-07 | NEI2KY300045 | 364227 | 863410 | 2.17E+04 | 2.17E+04 |
| 4.7E-07 | NEI2MIN0081 | 422840 | 830448 | 1.16E+04 | 1.16E+04 |
| 4.7E-07 | NEI2MIN3023 | 422836 | 830544 | 3.11E+04 | 3.11E+04 |
| 4.7E-07 | NEI2MIN5810 | 421647 | 834839 | 3.40E+01 | 3.40E+01 |
| 4.7E-07 | NEI2MIN6857 | 422806 | 825913 | 1.92E+04 | 1.92E+04 |
| 4.7E-07 | NEI2MIN6858 | 422753 | 825948 | 4.56E+03 | 4.56E+03 |
| 4.7E-07 | NEI2MIN6937 | 421359 | 834409 | 3.27E+02 | 3.27E+02 |
| 4.7E-07 | NEI2MIN7048 | 424857 | 825844 | 6.65E+03 | 6.65E+03 |
| 4.7E-07 | NEI2MN700294 | 445205 | 931020 | 6.40E+03 | 6.40E+03 |
| 4.7E-07 | NEI2MO071019 | 382922 | 904542 | 8.62E+03 | 8.62E+03 |
| 4.7E-07 | NEI2MO071132 | 383417 | 910212 | 1.79E+04 | 1.79E+04 |
| 4.7E-07 | NEI2MO077236 | 371304 | 931738 | 2.56E+03 | 2.56E+03 |
| 4.7E-07 | NEI2MO115005 | 394220 | 925707 | 7.74E+02 | 7.74E+02 |
| 4.7E-07 | NEI2MO1489 | 384635 | 902152 | 1.99E+04 | 1.99E+04 |
| 4.7E-07 | NEI2MO183018 | 384325 | 904253 | 6.92E+04 | 6.92E+04 |
| 4.7E-07 | NEI2MO189278 | 383203 | 902636 | 2.57E+03 | 2.57E+03 |
| 4.7E-07 | NEI2MO510094 | 383305 | 901547 | 2.57E+03 | 2.57E+03 |
| 4.7E-07 | NEI2NC00071 | 360354 | 801338 | 2.74E+00 | 2.28E+01 |
| 4.7E-07 | NEI2OK5092 | 344715 | 964024 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NEI2RIAIR13 | 415655 | 712757 | 2.62E+03 | 2.62E+03 |
| 4.7E-07 | NEI2RIAIR152 | 414729 | 712405 | 2.91E+03 | 2.91E+03 |
| 4.7E-07 | NEI2RIAIR19 | 414414 | 712647 | 1.60E+03 | 6.86E+03 |
| 4.7E-07 | NEI2RIAIR224 | 420033 | 713151 | 1.41E+02 | 1.41E+02 |
| 4.7E-07 | NEI2RIAIR245 | 414638 | 712534 | 2.43E+03 | 2.43E+03 |
| 4.7E-07 | NEI2RIAIR325 | 415605 | 712657 | 1.51E+02 | 1.25E+03 |
| 4.7E-07 | NEI2RIAIR354 | 414742 | 712912 | 1.50E+01 | 1.50E+01 |
| 4.7E-07 | NEI2RIAIR355 | 415232 | 712317 | 3.48E+03 | 3.48E+03 |
| 4.7E-07 | NEI2RIAIR409 | 414354 | 712645 | 1.55E+03 | 1.55E+03 |
| 4.7E-07 | NEI2RIAIR475 | 414901 | 712648 | 3.87E+03 | 3.87E+03 |
| 4.7E-07 | NEI2RIAIR673 | 414825 | 712430 | 1.57E+03 | 1.57E+03 |
| 4.7E-07 | NEI2RIAIR717 | 414946 | 712214 | 1.04E+03 | 1.04E+03 |
| 4.7E-07 | NEI2RIAIR74 | 414909 | 712229 | 4.85E+01 | 4.85E+01 |
| 4.7E-07 | NEI2RIAIR740 | 414725 | 712412 | 4.83E+01 | 4.83E+01 |
| 4.7E-07 | NEI2RIAIR748 | 414449 | 712655 | 2.72E+02 | 2.72E+02 |
| 4.7E-07 | NEI2RIAIR811 | 414853 | 712630 | 1.85E+03 | 1.85E+03 |
| 4.7E-07 | NEI2RIAIR874 | 415221 | 712432 | 6.45E+03 | 6.45E+03 |
| 4.7E-07 | NEI2RIAIR987 | 414949 | 712551 | 5.67E+03 | 5.67E+03 |
| 4.7E-07 | NEI2RIIR1109 | 415244 | 712354 | 5.56E+03 | 5.56E+03 |
| 4.7E-07 | NEI2RIIR1110 | 414851 | 712630 | 6.45E+02 | 6.45E+02 |
| 4.7E-07 | NEI2RIIR1230 | 415218 | 712444 | 2.41E+04 | 2.41E+04 |
| 4.7E-07 | NEI2RIIR1266 | 414745 | 712844 | 3.52E+03 | 3.52E+03 |
| 4.7E-07 | NEI2RIIR1483 | 415126 | 712042 | 1.25E+02 | 1.25E+02 |
| 4.7E-07 | NEI2RIIR1660 | 415312 | 712412 | 8.44E+03 | 8.44E+03 |
| 4.7E-07 | NEI2RIIR1831 | 415152 | 712406 | 5.26E+03 | 5.26E+03 |
| 4.7E-07 | NEI2RIIR1838 | 415300 | 712258 | 6.37E+03 | 6.37E+03 |
| 4.7E-07 | NEI2RIIR2579 | 414503 | 712616 | 4.90E+03 | 4.90E+03 |
| 4.7E-07 | NEI2RIIR2703 | 414803 | 712618 | 5.16E+03 | 5.16E+03 |
| 4.7E-07 | NEI2RIIR2874 | 414930 | 712816 | 5.10E+03 | 5.10E+03 |
| 4.7E-07 | NEI2RIIR3014 | 415404 | 712341 | 1.18E+04 | 1.18E+04 |
| 4.7E-07 | NEI2RIIR3168 | 414822 | 712550 | 1.00E+03 | 1.00E+03 |
| 4.7E-07 | NEI2RIIR3264 | 415312 | 712258 | 9.38E+02 | 9.38E+02 |
| 4.7E-07 | NEI2RIIR3506 | 414741 | 712426 | 1.27E+03 | 1.27E+03 |
| 4.7E-07 | NEI2RIIR3542 | 414729 | 712401 | 1.63E+04 | 1.63E+04 |
| 4.7E-07 | NEI2RIIR3572 | 415021 | 712512 | 2.82E+01 | 2.82E+01 |
| 4.7E-07 | NEI2RIIR3616 | 414005 | 711640 | 1.52E+03 | 1.52E+03 |
| 4.7E-07 | NEI2SC0-0175 | 345818 | 815929 | 2.10E+03 | 2.10E+03 |
| 4.7E-07 | NEI2SC0-0266 | 345649 | 815917 | 7.23E+02 | 6.01E+03 |
| 4.7E-07 | NEI2TX11369 | 324914 | 965035 | 1.25E+04 | 1.25E+04 |
| 4.7E-07 | NEI2WI243310 | 425908 | 875451 | 1.20E+04 | 1.20E+04 |
| 4.7E-07 | NEIART$10939 | 361121 | 940635 | 5.44E+04 | 5.44E+04 |
| 4.7E-07 | NEICA00160 | 374432 | 1221253 | 4.50E+03 | 4.50E+03 |
| 4.7E-07 | NEICA013629 | 375547 | 1220133 | 1.91E+02 | 1.59E+03 |
| 4.7E-07 | NEICA0333180 | 385533 | 1223654 | 2.08E+02 | 1.73E+03 |
| 4.7E-07 | NEICA0333190 | 390246 | 1225454 | 3.82E+02 | 3.17E+03 |
| 4.7E-07 | NEICA0371157 | 340260 | 1181352 | 3.08E+01 | 3.08E+01 |
| 4.7E-07 | NEICA0371160 | 335243 | 1180122 | 1.90E+03 | 1.90E+03 |
| 4.7E-07 | NEICA0371195 | 340860 | 1181916 | 3.48E+02 | 3.48E+02 |
| 4.7E-07 | NEICA0371208 | 334904 | 1181103 | 8.97E+01 | 7.45E+02 |
| 4.7E-07 | NEICA0371215 | 335654 | 1180404 | 1.10E+03 | 1.10E+03 |
| 4.7E-07 | NEICA0371244 | 341258 | 1183542 | 1.15E+03 | 1.15E+03 |
| 4.7E-07 | NEICA0371308 | 340260 | 1181352 | 4.17E+01 | 4.17E+01 |
| 4.7E-07 | NEICA0371319 | 340224 | 1180828 | 4.17E-01 | 4.17E-01 |
| 4.7E-07 | NEICA0371347 | 335956 | 1181848 | 3.27E+01 | 3.27E+01 |
| 4.7E-07 | NEICA0371361 | 335553 | 1182434 | 2.55E+03 | 2.55E+03 |
| 4.7E-07 | NEICA0371364 | 335256 | 1180057 | 3.43E+02 | 3.43E+02 |
| 4.7E-07 | NEICA0371372 | 341035 | 1181818 | 1.89E+02 | 1.89E+02 |
| 4.7E-07 | NEICA0371378 | 335950 | 1181237 | 1.61E+03 | 1.61E+03 |
| 4.7E-07 | NEICA0371384 | 340224 | 1184128 | 1.90E+02 | 1.42E+03 |
| 4.7E-07 | NEICA0371392 | 335135 | 1180923 | 1.44E+02 | 1.20E+03 |
| 4.7E-07 | NEICA0371508 | 341126 | 1183551 | 5.52E+01 | 4.59E+02 |
| 4.7E-07 | NEICA0371551 | 335348 | 1180209 | 3.43E+02 | 3.43E+02 |
| 4.7E-07 | NEICA0371606 | 335548 | 1182324 | 5.10E+00 | 5.10E+00 |
| 4.7E-07 | NEICA0378 | 340712 | 1175516 | 1.28E+04 | 1.28E+04 |
| 4.7E-07 | NEICA0592053 | 334160 | 1175104 | 4.10E+03 | 4.10E+03 |
| 4.7E-07 | NEICA0592066 | 335132 | 1175014 | 2.58E+03 | 2.58E+03 |
| 4.7E-07 | NEICA0592131 | 334312 | 1174952 | 2.93E+04 | 1.79E+05 |
| 4.7E-07 | NEICA06029F0 | 345529 | 1175328 | 1.43E+02 | 2.11E+02 |
| 4.7E-07 | NEICA0672219 | 383040 | 1212225 | 1.77E+03 | 1.77E+03 |
| 4.7E-07 | NEICA0672435 | 383049 | 1212822 | 8.36E+02 | 8.36E+02 |
| 4.7E-07 | NEICA0712392 | 351555 | 1164123 | 4.66E+01 | 3.87E+02 |
| 4.7E-07 | NEICA0712460 | 340246 | 1173153 | 6.39E+03 | 4.15E+04 |
| 4.7E-07 | NEICA0732551 | 325252 | 1170947 | 3.27E+02 | 3.27E+02 |
| 4.7E-07 | NEICA0732603 | 323818 | 1170627 | 4.23E-01 | 2.64E+00 |
| 4.7E-07 | NEICA0732639 | 324847 | 1171306 | 1.56E-01 | 1.30E+00 |
| 4.7E-07 | NEICA0732675 | 330806 | 1171341 | 9.26E+02 | 7.70E+03 |
| 4.7E-07 | NEICA0732681 | 323745 | 1170605 | 1.98E+03 | 2.00E+03 |
| 4.7E-07 | NEICA0732740 | 324208 | 1171139 | 8.95E+03 | 8.96E+03 |
| 4.7E-07 | NEICA0732742 | 323927 | 1170549 | 1.84E-01 | 1.53E+00 |
| 4.7E-07 | NEICA0732901 | 324831 | 1165804 | 3.39E+03 | 3.39E+03 |
| 4.7E-07 | NEICA0732960 | 324901 | 1165854 | 1.37E+03 | 1.14E+04 |
| 4.7E-07 | NEICA0732967 | 331254 | 1172352 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NEICA0732968 | 324133 | 1170822 | 2.10E-01 | 1.31E+00 |
| 4.7E-07 | NEICA0732973 | 330616 | 1171259 | 2.69E+02 | 2.92E+02 |
| 4.7E-07 | NEICA0732981 | 324927 | 1165928 | 1.80E+03 | 1.50E+04 |
| 4.7E-07 | NEICA0733011 | 324123 | 1170733 | 5.34E-01 | 4.43E+00 |
| 4.7E-07 | NEICA0733188 | 323536 | 1170315 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NEICA0733201 | 325248 | 1170659 | 1.45E+01 | 9.04E+01 |
| 4.7E-07 | NEICA0733205 | 324057 | 1170729 | 5.67E+00 | 3.53E+01 |
| 4.7E-07 | NEICA0733211 | 324018 | 1171010 | 4.17E+00 | 2.60E+01 |
| 4.7E-07 | NEICA0733419 | 324201 | 1171431 | 3.78E-02 | 2.36E-01 |
| 4.7E-07 | NEICA0733422 | 325045 | 1165816 | 1.05E-01 | 6.53E-01 |
| 4.7E-07 | NEICA0733441 | 324631 | 1170421 | 2.80E+01 | 1.89E+02 |
| 4.7E-07 | NEICA0773887 | 374318 | 1212956 | 1.92E-01 | 1.59E+00 |
| 4.7E-07 | NEICA0834298 | 342614 | 1195038 | 1.50E+03 | 4.36E+03 |
| 4.7E-07 | NEICA0834316 | 343556 | 1202737 | 2.82E+02 | 8.23E+02 |
| 4.7E-07 | NEICA0834319 | 342321 | 1192860 | 4.29E+02 | 1.25E+03 |
| 4.7E-07 | NEICA0834320 | 342903 | 1200225 | 1.23E+01 | 1.02E+02 |
| 4.7E-07 | NEICA0838003 | 344128 | 1200213 | 2.09E+03 | 1.74E+04 |
| 4.7E-07 | NEICA0838009 | 342549 | 1195159 | 1.01E+02 | 8.43E+02 |
| 4.7E-07 | NEICA0838012 | 344128 | 1200213 | 1.71E+02 | 1.42E+03 |
| 4.7E-07 | NEICA0838013 | 342549 | 1195159 | 1.78E+02 | 1.48E+03 |
| 4.7E-07 | NEICA0838016 | 344328 | 1202605 | 2.39E+03 | 7.15E+03 |
| 4.7E-07 | NEICA0838999 | 340050 | 1194444 | 1.58E+03 | 4.61E+03 |
| 4.7E-07 | NEICA0854805 | 372232 | 1215513 | 5.52E+01 | 5.52E+01 |
| 4.7E-07 | NEICA0854846 | 372316 | 1215423 | 2.21E+03 | 2.21E+03 |
| 4.7E-07 | NEICA0955098 | 381619 | 1215916 | 6.42E+03 | 6.42E+03 |
| 4.7E-07 | NEICA1014302 | 363050 | 1193307 | 1.64E+00 | 8.85E+00 |
| 4.7E-07 | NEICA1114712 | 341611 | 1184307 | 2.09E+02 | 1.29E+03 |
| 4.7E-07 | NEICA1115531 | 340637 | 1190619 | 1.00E+02 | 1.00E+02 |
| 4.7E-07 | NEICA1115663 | 341946 | 1190015 | 3.39E+00 | 2.81E+01 |
| 4.7E-07 | NEICA1115692 | 341617 | 1184315 | 5.00E+00 | 4.16E+01 |
| 4.7E-07 | NEICA1115697 | 341643 | 1185427 | 8.91E-02 | 7.40E-01 |
| 4.7E-07 | NEICO0048 | 381354 | 1043644 | 5.62E+01 | 4.67E+02 |
| 4.7E-07 | NEICO0050996 | 393719 | 1045916 | 5.18E+01 | 5.18E+01 |
| 4.7E-07 | NEICO0310511 | 394233 | 1045928 | 5.11E+02 | 4.25E+03 |
| 4.7E-07 | NEICO0623 | 394818 | 1045842 | 2.57E+03 | 2.57E+03 |
| 4.7E-07 | NEICO0632 | 400821 | 1050739 | 1.93E+03 | 1.93E+03 |
| 4.7E-07 | NEICO1768 | 394100 | 1045923 | 5.85E+01 | 5.85E+01 |
| 4.7E-07 | NEICTT$622 | 411728 | 725522 | 1.52E+04 | 1.52E+04 |
| 4.7E-07 | NEIFL0250677 | 254823 | 801735 | 1.55E+03 | 1.55E+03 |
| 4.7E-07 | NEIFL1010335 | 281633 | 823726 | 1.24E+03 | 1.24E+03 |
| 4.7E-07 | NEIFL1030098 | 274856 | 824504 | 4.70E+02 | 4.70E+02 |
| 4.7E-07 | NEIFL1030416 | 275211 | 824303 | 2.19E+04 | 2.19E+04 |
| 4.7E-07 | NEIFL1030447 | 275231 | 824357 | 6.80E+02 | 6.80E+02 |
| 4.7E-07 | NEIFLR023003 | 301029 | 823431 | 1.09E+01 | 1.09E+01 |
| 4.7E-07 | NEIFLR083013 | 291305 | 820835 | 9.07E+00 | 9.07E+00 |
| 4.7E-07 | NEIIAES0713f | 402521 | 912444 | 5.44E+03 | 4.52E+04 |
| 4.7E-07 | NEIIART$7942 | 414303 | 930235 | 1.20E-03 | 1.20E-03 |
| 4.7E-07 | NEIIAT$7932 | 412449 | 950203 | 3.59E+04 | 2.33E+05 |
| 4.7E-07 | NEIIAT$8120 | 403754 | 911809 | 1.27E+03 | 1.27E+03 |
| 4.7E-07 | NEIIL0075859 | 421504 | 885234 | 3.70E+02 | 3.07E+03 |
| 4.7E-07 | NEIIL0115886 | 412315 | 892726 | 7.12E+04 | 7.12E+04 |
| 4.7E-07 | NEIIL031195A | 420136 | 874711 | 6.49E+04 | 6.49E+04 |
| 4.7E-07 | NEIIL03142 | 420108 | 874735 | 2.38E+04 | 2.38E+04 |
| 4.7E-07 | NEIIL0316063 | 412955 | 874055 | 6.57E+03 | 5.46E+04 |
| 4.7E-07 | NEIIL0316147 | 415628 | 875123 | 2.23E+02 | 1.85E+03 |
| 4.7E-07 | NEIIL0316332 | 415118 | 875127 | 6.02E+03 | 6.02E+03 |
| 4.7E-07 | NEIIL0316389 | 415230 | 875203 | 1.59E+04 | 1.59E+04 |
| 4.7E-07 | NEIIL0316435 | 420040 | 874316 | 8.61E+03 | 8.61E+03 |
| 4.7E-07 | NEIIL0316467 | 420223 | 874737 | 5.06E+04 | 5.06E+04 |
| 4.7E-07 | NEIIL0316542 | 414909 | 875147 | 2.19E+03 | 2.19E+03 |
| 4.7E-07 | NEIIL0316594 | 415659 | 875149 | 5.68E+04 | 5.68E+04 |
| 4.7E-07 | NEIIL0316639 | 420134 | 874254 | 1.68E+04 | 1.68E+04 |
| 4.7E-07 | NEIIL0316641 | 420108 | 874308 | 7.03E+03 | 7.03E+03 |
| 4.7E-07 | NEIIL0316686 | 420844 | 875111 | 6.53E+03 | 6.53E+03 |
| 4.7E-07 | NEIIL0316702 | 420108 | 874707 | 2.01E+03 | 2.01E+03 |
| 4.7E-07 | NEIIL0316720 | 420108 | 874652 | 6.67E+03 | 6.67E+03 |
| 4.7E-07 | NEIIL0316721 | 420058 | 874655 | 7.26E+02 | 7.26E+02 |
| 4.7E-07 | NEIIL0316723 | 420044 | 874707 | 8.02E+02 | 6.66E+03 |
| 4.7E-07 | NEIIL0316747 | 415601 | 875059 | 7.72E+02 | 7.72E+02 |
| 4.7E-07 | NEIIL0316842 | 420011 | 880027 | 1.00E+03 | 1.00E+03 |
| 4.7E-07 | NEIIL0316995 | 415302 | 873858 | 3.43E+00 | 2.85E+01 |
| 4.7E-07 | NEIIL0317010 | 415619 | 874247 | 2.12E+04 | 2.12E+04 |
| 4.7E-07 | NEIIL0317020 | 414826 | 874157 | 1.38E+04 | 1.15E+05 |
| 4.7E-07 | NEIIL0317093 | 414856 | 874250 | 9.26E+03 | 9.26E+03 |
| 4.7E-07 | NEIIL0317139 | 415316 | 874002 | 8.27E+03 | 8.27E+03 |
| 4.7E-07 | NEIIL0317140 | 415249 | 873927 | 1.37E+03 | 1.37E+03 |
| 4.7E-07 | NEIIL0317197 | 415547 | 874031 | 8.51E+03 | 8.51E+03 |
| 4.7E-07 | NEIIL0317202 | 415734 | 874028 | 2.07E+02 | 2.07E+02 |
| 4.7E-07 | NEIIL0317366 | 414857 | 874318 | 3.28E+03 | 2.73E+04 |
| 4.7E-07 | NEIIL0317662 | 415454 | 874420 | 3.09E+03 | 3.09E+03 |
| 4.7E-07 | NEIIL0317669 | 415620 | 874117 | 1.47E+04 | 1.47E+04 |
| 4.7E-07 | NEIIL0317689 | 415853 | 874538 | 1.72E+04 | 1.72E+04 |
| 4.7E-07 | NEIIL043020A | 415420 | 880610 | 5.77E+04 | 5.77E+04 |
| 4.7E-07 | NEIIL043095A | 414760 | 875800 | 2.54E+04 | 2.54E+04 |
| 4.7E-07 | NEIIL0435ALQ | 415526 | 875928 | 1.72E+04 | 1.72E+04 |
| 4.7E-07 | NEIIL0437946 | 415530 | 880507 | 6.12E+03 | 6.12E+03 |
| 4.7E-07 | NEIIL0438058 | 414760 | 880230 | 2.40E+02 | 1.99E+03 |
| 4.7E-07 | NEIIL0438068 | 414742 | 880236 | 4.97E+03 | 4.97E+03 |
| 4.7E-07 | NEIIL0438080 | 415837 | 875913 | 3.76E+02 | 3.76E+02 |
| 4.7E-07 | NEIIL0438118 | 415816 | 875633 | 3.98E+03 | 3.98E+03 |
| 4.7E-07 | NEIIL0458147 | 393556 | 874137 | 1.36E+04 | 1.13E+05 |
| 4.7E-07 | NEIIL0638273 | 412260 | 882500 | 1.08E+04 | 9.00E+04 |
| 4.7E-07 | NEIIL089080A | 415946 | 881735 | 1.39E+04 | 1.39E+04 |
| 4.7E-07 | NEIIL0898477 | 420423 | 881746 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NEIIL0978631 | 421134 | 880700 | 3.77E+04 | 3.77E+04 |
| 4.7E-07 | NEIIL0978727 | 421532 | 875913 | 1.45E+04 | 1.45E+04 |
| 4.7E-07 | NEIIL0978767 | 421622 | 875419 | 7.07E+03 | 7.07E+03 |
| 4.7E-07 | NEIIL0998825 | 410737 | 884753 | 7.49E+02 | 7.49E+02 |
| 4.7E-07 | NEIIL111005A | 421013 | 881756 | 1.61E+04 | 1.61E+04 |
| 4.7E-07 | NEIIL1110AAD | 422811 | 882605 | 1.20E+04 | 1.20E+04 |
| 4.7E-07 | NEIIL1118956 | 422850 | 881833 | 7.29E+03 | 7.29E+03 |
| 4.7E-07 | NEIIL1118985 | 421157 | 881359 | 2.04E+03 | 1.69E+04 |
| 4.7E-07 | NEIIL1118996 | 421501 | 881833 | 1.16E+04 | 1.16E+04 |
| 4.7E-07 | NEIIL1118998 | 421441 | 881826 | 6.86E+03 | 6.86E+03 |
| 4.7E-07 | NEIIL1119043 | 421416 | 881854 | 7.64E+03 | 7.64E+03 |
| 4.7E-07 | NEIIL18396 | 400825 | 873502 | 3.18E+03 | 3.18E+03 |
| 4.7E-07 | NEIIL1839883 | 400736 | 873843 | 2.16E+04 | 2.16E+04 |
| 4.7E-07 | NEIIL1839900 | 400739 | 873839 | 2.97E+04 | 2.97E+04 |
| 4.7E-07 | NEIIL2010AZW | 421542 | 890543 | 1.78E+04 | 1.78E+04 |
| 4.7E-07 | NEIIL227 | 422727 | 890325 | 1.49E+02 | 1.49E+02 |
| 4.7E-07 | NEIIL241 | 421309 | 890130 | 2.08E+04 | 2.08E+04 |
| 4.7E-07 | NEIIL91 | 412634 | 881208 | 1.07E+04 | 1.07E+04 |
| 4.7E-07 | NEIILT$9050 | 420246 | 875924 | 1.24E+02 | 1.24E+02 |
| 4.7E-07 | NEIILT$9130 | 420135 | 874241 | 2.32E+04 | 2.32E+04 |
| 4.7E-07 | NEIILT$9235 | 415648 | 882344 | 7.86E+03 | 7.86E+03 |
| 4.7E-07 | NEIIN0010001 | 404912 | 845624 | 1.13E+05 | 1.13E+05 |
| 4.7E-07 | NEIIN00119 | 395324 | 860339 | 8.80E+01 | 8.80E+01 |
| 4.7E-07 | NEIIN00247 | 413708 | 873129 | 8.05E+03 | 8.05E+03 |
| 4.7E-07 | NEIIN00297 | 394608 | 860642 | 2.92E+04 | 2.92E+04 |
| 4.7E-07 | NEIIN0390015 | 414132 | 855939 | 1.82E+04 | 1.82E+04 |
| 4.7E-07 | NEIIN039144 | 414201 | 855948 | 6.02E+03 | 6.02E+03 |
| 4.7E-07 | NEIIN051153 | 382011 | 872024 | 6.93E+03 | 6.93E+03 |
| 4.7E-07 | NEIIN0890254 | 413629 | 872826 | 3.05E+02 | 3.05E+02 |
| 4.7E-07 | NEIIN555 | 412112 | 862001 | 1.74E+04 | 1.74E+04 |
| 4.7E-07 | NEIKS00075 | 373901 | 971611 | 1.12E+05 | 1.12E+05 |
| 4.7E-07 | NEIKS00165 | 374000 | 972235 | 3.01E+04 | 3.01E+04 |
| 4.7E-07 | NEIKS325 | 370239 | 953724 | 8.16E+04 | 6.78E+05 |
| 4.7E-07 | NEIKST$10304 | 373954 | 972541 | 1.65E+04 | 1.65E+04 |
| 4.7E-07 | NEIKST$10326 | 373850 | 972427 | 2.91E+04 | 2.91E+04 |
| 4.7E-07 | NEIKY009210 | 365932 | 855707 | 3.28E+03 | 3.28E+03 |
| 4.7E-07 | NEIKY1131 | 365811 | 862831 | 1.79E+05 | 1.79E+05 |
| 4.7E-07 | NEIKY1145 | 380354 | 844321 | 1.38E+02 | 1.15E+03 |
| 4.7E-07 | NEIKY719 | 380342 | 845540 | 5.65E+04 | 5.65E+04 |
| 4.7E-07 | NEIKY829 | 380237 | 842813 | 3.82E+03 | 3.82E+03 |
| 4.7E-07 | NEIKY987 | 365058 | 865400 | 1.94E+04 | 1.94E+04 |
| 4.7E-07 | NEIKYT$5489 | 380445 | 843202 | 1.01E+04 | 1.01E+04 |
| 4.7E-07 | NEILA1150010 | 310255 | 931231 | 9.77E+00 | 2.48E+01 |
| 4.7E-07 | NEIMI027N588 | 414753 | 860306 | 2.31E+01 | 2.31E+01 |
| 4.7E-07 | NEIMI049N112 | 430804 | 834302 | 1.24E+03 | 1.24E+03 |
| 4.7E-07 | NEIMI065A163 | 424037 | 843146 | 7.77E+03 | 7.77E+03 |
| 4.7E-07 | NEIMI161N505 | 421342 | 834130 | 2.61E+02 | 2.61E+02 |
| 4.7E-07 | NEIMI163A895 | 422216 | 832113 | 3.65E+03 | 3.65E+03 |
| 4.7E-07 | NEIMI163N024 | 421728 | 831725 | 4.25E+03 | 4.25E+03 |
| 4.7E-07 | NEIMIA0155 | 423831 | 851832 | 2.49E+01 | 2.49E+01 |
| 4.7E-07 | NEIMIA2416 | 425340 | 853255 | 3.31E+03 | 3.31E+03 |
| 4.7E-07 | NEIMIA2447 | 425440 | 854026 | 7.23E+02 | 6.00E+03 |
| 4.7E-07 | NEIMIA2931 | 423610 | 835557 | 3.06E+04 | 3.06E+04 |
| 4.7E-07 | NEIMIB1904 | 431313 | 861525 | 6.09E+03 | 6.09E+03 |
| 4.7E-07 | NEIMIB2289 | 415344 | 840102 | 1.79E+04 | 1.79E+04 |
| 4.7E-07 | NEIMIB4096 | 415053 | 853921 | 9.61E+03 | 9.61E+03 |
| 4.7E-07 | NEIMIB6220 | 423544 | 825110 | 1.25E+04 | 1.25E+04 |
| 4.7E-07 | NEIMIB7018 | 422854 | 832855 | 1.96E+03 | 1.96E+03 |
| 4.7E-07 | NEIMIM4403 | 421943 | 832507 | 4.21E+04 | 4.21E+04 |
| 4.7E-07 | NEIMIM4607 | 421131 | 831003 | 6.59E+03 | 6.59E+03 |
| 4.7E-07 | NEIMIN3303 | 421820 | 851533 | 2.14E+03 | 2.14E+03 |
| 4.7E-07 | NEIMIN6173 | 451748 | 851501 | 8.22E+00 | 6.83E+01 |
| 4.7E-07 | NEIMIN6646 | 430002 | 841224 | 7.65E+03 | 7.65E+03 |
| 4.7E-07 | NEIMIN6660 | 423049 | 830638 | 1.30E+03 | 1.30E+03 |
| 4.7E-07 | NEIMIT$7376 | 423259 | 825642 | 1.62E+03 | 1.35E+04 |
| 4.7E-07 | NEIMIT$7475 | 415519 | 832206 | 2.37E+04 | 2.37E+04 |
| 4.7E-07 | NEIMN019264 | 445028 | 933543 | 6.86E+03 | 6.86E+03 |
| 4.7E-07 | NEIMN123294 | 445607 | 930433 | 2.15E+04 | 2.15E+04 |
| 4.7E-07 | NEIMN1429 | 441024 | 940245 | 4.94E+03 | 4.94E+03 |
| 4.7E-07 | NEIMN2713900 | 444706 | 933030 | 3.87E+03 | 3.87E+03 |
| 4.7E-07 | NEIMNT$8769 | 444940 | 931213 | 1.67E+04 | 1.67E+04 |
| 4.7E-07 | NEIMNT$8791 | 445056 | 933541 | 9.09E+04 | 7.55E+05 |
| 4.7E-07 | NEIMNT$8855 | 450500 | 932321 | 2.01E+04 | 2.01E+04 |
| 4.7E-07 | NEIMNT$8860 | 450610 | 931558 | 2.71E+04 | 2.71E+04 |
| 4.7E-07 | NEIMS025298 | 333530 | 883846 | 9.59E+00 | 7.97E+01 |
| 4.7E-07 | NEINC0216 | 351231 | 805640 | 1.00E+02 | 1.00E+02 |
| 4.7E-07 | NEINCT$3034 | 351254 | 803128 | 4.09E+02 | 4.09E+02 |
| 4.7E-07 | NEINM0001 | 355135 | 1061824 | 3.86E+01 | 3.86E+01 |
| 4.7E-07 | NEINM0031 | 321619 | 1065458 | 4.89E+04 | 4.89E+04 |
| 4.7E-07 | NEINY1957 | 404200 | 735848 | 4.59E+04 | 4.59E+04 |
| 4.7E-07 | NEINY1998 | 430448 | 751500 | 2.26E+04 | 2.26E+04 |
| 4.7E-07 | NEINY2054 | 405512 | 735136 | 3.51E+03 | 3.51E+03 |
| 4.7E-07 | NEINY8265400 | 431312 | 772436 | 9.72E+02 | 9.72E+02 |
| 4.7E-07 | NEIOH0351982 | 413156 | 813254 | 3.22E+03 | 2.67E+04 |
| 4.7E-07 | NEIOH0829700 | 394902 | 840213 | 3.43E+02 | 2.85E+03 |
| 4.7E-07 | NEIOH0857730 | 394856 | 841048 | 1.93E+04 | 1.93E+04 |
| 4.7E-07 | NEIOH0857770 | 394745 | 840802 | 7.72E+03 | 7.72E+03 |
| 4.7E-07 | NEIOH17077 | 412916 | 814349 | 6.54E+03 | 5.43E+04 |
| 4.7E-07 | NEIOHRR255 | 394915 | 840024 | 1.16E+04 | 1.16E+04 |
| 4.7E-07 | NEIOHRR343 | 400223 | 841157 | 9.59E+03 | 7.97E+04 |
| 4.7E-07 | NEIOHRR364 | 395804 | 841155 | 9.65E+03 | 9.65E+03 |
| 4.7E-07 | NEIOHRR385 | 394654 | 841053 | 1.62E+04 | 1.62E+04 |
| 4.7E-07 | NEIOHRR386 | 394611 | 840857 | 2.06E+03 | 1.71E+04 |
| 4.7E-07 | NEIOHRR501 | 393739 | 841419 | 5.48E+03 | 4.56E+04 |
| 4.7E-07 | NEIOHRR577 | 394727 | 841135 | 2.01E+04 | 2.01E+04 |
| 4.7E-07 | NEIOHT$6567 | 394547 | 841047 | 6.17E+03 | 5.12E+04 |
| 4.7E-07 | NEIOHT$6598 | 393912 | 841436 | 2.12E+04 | 2.12E+04 |
| 4.7E-07 | NEIOK1020 | 361244 | 955222 | 5.50E+04 | 3.15E+05 |
| 4.7E-07 | NEIOK4211 | 360923 | 955817 | 9.87E+02 | 8.20E+03 |
| 4.7E-07 | NEIPA003347 | 403416 | 795149 | 3.97E+01 | 3.30E+02 |
| 4.7E-07 | NEIPA1014907 | 395445 | 751358 | 1.78E-02 | 1.48E-01 |
| 4.7E-07 | NEIPA12304-3 | 415208 | 790901 | 2.66E+04 | 2.66E+04 |
| 4.7E-07 | NEIPA13304-3 | 395804 | 764517 | 2.99E+04 | 2.99E+04 |
| 4.7E-07 | NEIPA14-1682 | 401512 | 751647 | 2.70E+03 | 2.70E+03 |
| 4.7E-07 | NEIPA2187 | 410711 | 784540 | 7.98E+03 | 2.41E+04 |
| 4.7E-07 | NEIPA2244 | 400135 | 750154 | 3.86E+03 | 3.86E+03 |
| 4.7E-07 | NEIPA23-0419 | 400908 | 750048 | 1.51E+04 | 1.51E+04 |
| 4.7E-07 | NEIPA23-1498 | 402456 | 752317 | 9.26E+02 | 9.26E+02 |
| 4.7E-07 | NEIPA23-2230 | 415918 | 763056 | 1.54E+03 | 1.54E+03 |
| 4.7E-07 | NEIPA23-2947 | 400626 | 793503 | 1.02E+05 | 1.02E+05 |
| 4.7E-07 | NEIPA25-0932 | 414610 | 780500 | 3.17E+03 | 3.17E+03 |
| 4.7E-07 | NEIPA25-1054 | 401751 | 792330 | 5.56E+03 | 5.56E+03 |
| 4.7E-07 | NEIPA25-1185 | 395115 | 794436 | 2.22E+03 | 2.22E+03 |
| 4.7E-07 | NEIPA25-1355 | 414760 | 783800 | 2.49E+02 | 2.49E+02 |
| 4.7E-07 | NEIPAT$1635 | 412000 | 802700 | 7.14E+04 | 7.14E+04 |
| 4.7E-07 | NEIPAT$1693 | 420015 | 801405 | 1.15E+03 | 1.15E+03 |
| 4.7E-07 | NEIPAT$2047 | 395211 | 751915 | 6.80E+03 | 6.80E+03 |
| 4.7E-07 | NEIRCA303707 | 372344 | 1220654 | 1.35E+03 | 1.35E+03 |
| 4.7E-07 | NEIRCA310521 | 373047 | 1221531 | 4.82E+03 | 4.82E+03 |
| 4.7E-07 | NEIRCA310581 | 374633 | 1221425 | 1.80E+02 | 1.80E+02 |
| 4.7E-07 | NEIRCA310599 | 374601 | 1221308 | 8.27E+02 | 8.27E+02 |
| 4.7E-07 | NEIRCA311021 | 372245 | 1215819 | 7.32E+00 | 7.32E+00 |
| 4.7E-07 | NEIRCA311226 | 380048 | 1220217 | 3.31E+03 | 3.31E+03 |
| 4.7E-07 | NEIRI01004 | 415145 | 712038 | 1.05E+02 | 1.05E+02 |
| 4.7E-07 | NEIRIAMDI643 | 410320 | 942036 | 8.20E+03 | 6.81E+04 |
| 4.7E-07 | NEIRMN300066 | 450349 | 931606 | 4.31E+03 | 4.31E+03 |
| 4.7E-07 | NEIRMN301074 | 445718 | 931336 | 9.87E+03 | 9.87E+03 |
| 4.7E-07 | NEIRMN500041 | 445346 | 942248 | 5.24E+03 | 5.24E+03 |
| 4.7E-07 | NEIROR686964 | 453001 | 1224922 | 8.38E+02 | 8.38E+02 |
| 4.7E-07 | NEIRSC0-0021 | 341222 | 820736 | 8.26E-01 | 6.87E+00 |
| 4.7E-07 | NEIRSC156063 | 335643 | 810716 | 3.63E+01 | 3.63E+01 |
| 4.7E-07 | NEISCT$3360 | 340733 | 805213 | 8.28E+03 | 8.28E+03 |
| 4.7E-07 | NEISCT$3554 | 344131 | 823045 | 2.30E+04 | 2.30E+04 |
| 4.7E-07 | NEIT$FNP1184 | 453420 | 1223602 | 1.54E+04 | 1.54E+04 |
| 4.7E-07 | NEITN0470 | 350111 | 851750 | 1.60E+03 | 1.60E+03 |
| 4.7E-07 | NEITNT$5022 | 355725 | 834936 | 6.68E+04 | 6.68E+04 |
| 4.7E-07 | NEITXRDF0558 | 330016 | 971838 | 1.46E+04 | 1.46E+04 |
| 4.7E-07 | NEITXT$11144 | 323235 | 970222 | 9.38E+04 | 9.38E+04 |
| 4.7E-07 | NEITXT$11265 | 325540 | 964528 | 4.90E+03 | 4.07E+04 |
| 4.7E-07 | NEITXT$11375 | 325603 | 970555 | 1.24E+04 | 1.24E+04 |
| 4.7E-07 | NEITXT$11600 | 302332 | 952825 | 2.12E+04 | 2.12E+04 |
| 4.7E-07 | NEIUT0351664 | 405059 | 1115800 | 1.79E+03 | 1.79E+03 |
| 4.7E-07 | NEIUT10555 | 404152 | 1115403 | 1.83E+02 | 1.52E+03 |
| 4.7E-07 | NEIVA0470044 | 382811 | 780030 | 2.83E+03 | 2.83E+03 |
| 4.7E-07 | NEIVAT$2444 | 372953 | 773534 | 4.08E+04 | 3.39E+05 |
| 4.7E-07 | NEIWA0072 | 474031 | 1171159 | 5.44E+02 | 5.44E+02 |
| 4.7E-07 | NEIWA13120 | 475511 | 1221638 | 1.15E+05 | 1.15E+05 |
| 4.7E-07 | NEIWA14082 | 473348 | 1223758 | 6.07E+03 | 6.07E+03 |
| 4.7E-07 | NEIWI1314880 | 432352 | 881160 | 2.98E+03 | 2.98E+03 |
| 4.7E-07 | NEIWI1541294 | 424625 | 891757 | 2.55E+03 | 2.55E+03 |
| 4.7E-07 | NEIWI2410173 | 430855 | 880047 | 5.37E+03 | 5.37E+03 |
| 4.7E-07 | NEIWI2410368 | 430256 | 875457 | 1.32E+03 | 1.32E+03 |
| 4.7E-07 | NEIWI2419617 | 425202 | 875853 | 6.85E+03 | 6.85E+03 |
| 4.7E-07 | NEIWI2460526 | 432232 | 875258 | 2.09E+04 | 2.09E+04 |
| 4.7E-07 | NEIWI2520097 | 424452 | 874804 | 6.14E+03 | 6.14E+03 |
| 4.7E-07 | NEIWI2650061 | 424726 | 882322 | 3.11E+05 | 3.11E+05 |
| 4.7E-07 | NEIWI2680147 | 430509 | 881554 | 1.80E+04 | 1.80E+04 |
| 4.7E-07 | NEIWI2682381 | 430252 | 881060 | 1.33E+04 | 1.33E+04 |
| 4.7E-07 | NEIWI6030598 | 453238 | 920103 | 2.57E+04 | 2.57E+04 |
| 4.7E-07 | NEIWI7440095 | 453755 | 892339 | 6.74E+03 | 6.74E+03 |
| 4.7E-07 | NEIWIT$8642 | 445720 | 912222 | 4.32E+04 | 4.32E+04 |
| 4.7E-07 | NEIWV0110009 | 382528 | 822555 | 3.59E+00 | 2.98E+01 |

1 Fields omitted for this exhibit: Chemical name = MC equivalent; Facility ID Number (sequential; irrelevant as long as the numbering is consistent for each facility across all input files); Location (all halogenated solvent cleaning facilities are given a value of 1 for rural); Number of Emission Points (1 for all halogenated solvent cleaning facilities); Emission Point ID Number (1 for all halogenated solvent cleaning facilities); Vent Type (all halogenated solvent cleaning facilities are given a value of H for stack); Stack Height, Area, Vent Type, Diameter, Gas Exit Velocity, Gas Exit Temperature (see Exhibit C-1); Model Output Maps (all halogenated solvent cleaning facilities are given a value of ‘N – No’); Each Ring (all halogenated solvent cleaning facilities are given a value of ‘N – No’).
2 In HEM-SCREEN, latitude and longitude are presented as DDMMSS, where DD is degrees, MM is minutes, SS is seconds.  Longitude is in degrees West.

3 We evaluated risks separately using the California EPA (CalEPA) URE for perchloroethylene (PCE) of 5.9 × 10-6 (μg/m3)-1 and a URE for PCE developed by EPA’s Office of Prevention, Pesticides and Toxic Substance (OPPTS) of 7.1 × 10-7 (μg/m3)-1.

4 MC = methylene chloride.

# Footnotes

The document Risk Assessment for the Halogenated Solvent Cleaning Source Category, prepared by ICF on August 4, 2006, has EPA docket document ID EPA-HQ-OAR-2002-0009-0022.  An updated risk assessment, Summary of Estimated Cancer Risks for the Halogenated Solvents Source Category using NEI 2002, was prepared on April 10, 2007 and has EPA docket document ID EPA-HQ-OAR-2002-0009-0133.

Ted Johnson and Jim Capel. 1992. A Monte Carlo Approach to Simulating Residential Occupancy Periods and Its Application to the General U.S. Population, EPA-450/3-92-011, U.S. Environmental Protection Agency, Research Triangle Park, N.C. Available in the docket for this rule.

A review of the data used in the 2007 Halogenated Solvents assessment (using 2002 NEI data) indicated that non-defaulted stack parameters were very similar to those used for the residual risk assessment based on the original risk assessment (using 1999 NEI data).

Risk Assessment for the Halogenated Solvent Cleaning Source Category at docket # OAR-2002-0009-0022

This risk assessment memo dated April 10, 2007, at docket # OAR-2002-0009-0133

US EPA, 1996.  Exposure Factors Handbook.  National Center for Environmental Assessment, Office of Research and Development.  Available online at http://www.epa.gov/ncea/efh/  Residence time data in Table 15-167.

Ted Johnson and Jim Capel. 1992. A Monte Carlo Approach to Simulating Residential Occupancy Periods and Its Application to the General U.S. Population, EPA-450/3-92-011, U.S. Environmental Protection Agency, Research Triangle Park, N.C. Available in the docket for this rule.

US Census Bureau, 2007.  Survey of Income and Program Participation.  Available online at http://www.sipp.census.gov/sipp/ .

US Census Bureau, 2007.  American Community Survey.  Available online at http://www.census.gov/acs/www/ .