LAAS Benefits Analysis

LAAS Efficiency, Safety, and Societal Benefits

October 31, 2004

Table of Contents

Introduction	3

Important Considerations for Interpreting Results	5

General Approach	9

Incremental Benefits	9

Scope and Key Assumptions	9

Validation of  Methodology and Data	10

Efficiency Benefits	11

Summary of Efficiency Benefits	11

Reduced Disruptions for Straight-in Precision Approaches	24

Reduced Disruptions with LAAS Takeoff Guidance	30

Benefits from LAAS-based Complex Procedures	32

Benefits Due to Elimination of ILS Critical Areas	36

Benefits for Closely Spaced Parallel Approaches	41

Qualitative Efficiency Benefits	45

Safety Benefits	49

Societal Benefits	54

Continuation of U.S. technology leadership in air navigation	55

International LGF and LAAS Avionics Sales Revenue	55

Noise Abatement and Mitigation	56

Reduced Impact on Environmentally Sensitive Areas	60

LAAS as a Complement to Homeland Security	61

LAAS and JPALS Providing Civilian and Military Compatibility	63

Expansion of Air Commerce to Smaller Communities	64

Increased Reliability of Air Service	64

LAAS Signal in the Vicinity of the 121 Studied Airports	66

Appendices	67

Appendix A:	Airports Included in This Study	67

Appendix B: 	Order of Installation of LAAS Ground Facilities	70

Appendix C: 	Derivation of Disruption Costs	75

Appendix D: 	Sensitivity Analyses	78

Appendix E:	Derivation of the Single Airport Delay Model	83

Appendix F:	Navigation Capabilities Baseline	88

Appendix G:	Potential LAAS Sites Outside of the 121 Airports	102

Appendix H:	LAAS Signal in the Vicinity of the 121 Studied Airports - Example	103

Appendix I:           LAAS Benefits Analysis Assumptions	105

Appendix J:           LAAS Efficiency Benefits by User Group	107

Appendix K:	Data Sources	117

Appendix L:	List of Acronyms	118

Appendix M:	Runway Utilization Analysis	120

Appendix N:	Analysis of the Downstream Effect of Delays	124

Appendix O:	Severe Weather Categories Eliminated From This Analsyis	128

Appendix P: 	Cargo ‘Box Value of Time’ by Airport	129

Appendix Q:	Government and Industry Contributors	132

Appendix R:	Number of ILSs Required to Achieve Equivalent LAAS Benefit	136

Notes and References	139

# Introduction

The Federal Aviation Administration (FAA) is transforming the navigation infrastructure of the National Airspace System (NAS), from a ground-based to a Global Positioning System (GPS)-based architecture.  Part of this transformation entails the acquisition of augmentation systems to improve the accuracy, reliability, and integrity of the GPS signals.  The Local Area Augmentation System (LAAS) is one of these systems, specifically designed to support aircraft operations in the terminal, approach, surface, and departure operational domains.

The FAA contracted with IBM Business Consulting Services to provide an independent analysis that estimates the benefits attributable to LAAS beyond those provided by existing and planned navigation services.  These benefits are estimated over a 20 year period (2009-2028), at 121 selected airports, and for five distinct user groups: major passenger airlines, regional passenger airlines, cargo carriers, corporate jet operators, and general aviation (GA) operators in Alaska.  This analysis serves as an update of previous studies    as well as a more comprehensive and detailed evaluation of contributions that can be expected from LAAS. The analysis is based on independent research, and is supported by inputs solicited from both service providers and airline industry representatives, including validation of methodology, data, and output.  The results of this analysis will be used to support the FAA, the airlines, and other stakeholders in their procurement and implementation decisions related to LAAS.

Benefits reported in the LAAS Benefits Analysis are those estimated to be achievable by LAAS relative to the established Navigation Capabilities Baseline, delivered to the FAA in November 2003.  Some of these LAAS benefits may be reduced or eliminated if significant enhancements of the navigation system infrastructure, beyond those established in the Baseline, were to be considered.  In particular, approximately 95% of the estimated benefits are associated directly or indirectly with the ability of LAAS to provide precision guidance service.  Since this type of service can also be achieved with the instrument landing system (ILS), the installation or upgrade of ILS at all runways estimated to receive LAAS benefits would substantially reduce these benefits.  The installation of over 100 new ILS systems, plus the upgrade of over 300 Cat I ILSs to Cat II/III capability, will be required in order to provide benefits similar to those calculated for the 121 LAAS installations studied in this report.  Decisions made by the FAA and the users about the preferred navigation alternative will be largely dependent on the lifecycle cost differential between installing either a single LAAS or one or more ILSs at each airport to achieve these benefits.

The first stage of the benefits analysis, completed in November 2003, involved the establishment of the navigation capabilities baseline against which all LAAS benefits would be measured.  The second stage, completed in December 2003, entailed determining the incremental capabilities provided by LAAS, above and beyond this baseline.  In February 2004, IBM delivered a Preliminary Findings report, which described a series of analyses conducted to estimate the monetized incremental benefits that can be expected from implementation of LAAS, relative to the baseline. In June 2004, IBM completed an update on the efficiency section of the February 2004 preliminary analysis of the LAAS benefits, and the findings were documented in a report.  In August 2004, IBM delivered the LAAS Safety and Societal Benefits report.  This final report includes descriptions of LAAS benefits for three areas; Efficiency, Safety and Societal.

### Efficiency Benefits

- Quantitative

  - Lower ceiling and visibility minima for straight-in approaches,

  - Improved takeoff guidance in low visibility conditions,

  - Improved ceiling and visibility minima for complex approaches,

  - Elimination of Instrument Landing System (ILS) critical areas, and

  - Increased capacity from closely spaced parallel approaches

- Qualitative

  - Increased capacity from variable glideslopes

  - Increased data capacity and integrity digital data uplinks

  - Increased capacity from airspace confliction resolution

  - Increased capacity and reduced minima through guided missed approaches

  - Increased airport situational awareness through precision guided surface navigation

### Safety Benefits

- Precision approach benefits

- Airport surface navigation benefits

### Societal Benefits

- Quantitative

  - Estimate of international LAAS Ground Facility (LGF) and LAAS avionics sales revenue to U.S. manufacturers

  - Analysis of increased reliability of air service

The quantitative societal benefits included in this report are speculative, and are included here only to illustrate the importance of the economic impact that LAAS may provide.  These quantitative societal benefit estimates are not incorporated into the total benefits derived from the efficiency and safety benefits analysis.

- Qualitative

  - Continuation and possible enhancement of U.S. technology leadership in air navigation

  - Noise abatement and mitigation

  - Reduced impact on environmentally sensitive areas

  - How LAAS complements Homeland Security

  - How LAAS and Joint Precision Approach and Landing System (JPALS) offer civilian and military compatibility

  - Expansion of air commerce to smaller communities

Table 1 shows the principal results of this analysis – the total 20-year discounted benefits estimated for all 121 airports.  These benefits, which included improvements in efficiency and safety, were determined to be $1.5 billion and $986 million for the 0% and 100% Wide Area Augmentation System (WAAS) equipage scenarios (as described in the General Approach section), respectively.

Table  1: Discounted 20-year LAAS Benefits – Best Estimate

|  | Efficiency | Safety | Total |
| --- | --- | --- | --- |
|  | Direct Operating Cost Savings | Passenger Time Savings |  |  |
| LAAS Benefits (Assuming 0% WAAS equipage) | $638,900,000 | $795,800,000 | $58,300,000 | $1,493,000,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $429,300,000 | $542,100,000 | $14,900,000 | $986,300,000 |

# Important Considerations for Interpreting Results

This section describes several important points about the estimates of LAAS benefits in this study.  These points are intended to highlight their significance to the study and to foster discussion of their treatment in the analysis.

- The benefits reported in this document do not include one potentially important economic impact of flight disruptions on cargo operations.  While, benefits studies typically include an estimate of the impact of flight disruptions on passengers in the form of Passenger Time Savings, the corollary of this in cargo operations, sometimes referred to as Box Value of Time, is often overlooked.  Much of the volume carried by air cargo operators, as well as the cargo carried on passenger flights, is highly time-sensitive, and thus the value of this cargo is significantly reduced by delays and other disruptions.  This was noted in a report on The National Economic Impact of Civil Aviation: “The key elements in all types of air cargo service are speed and reliability. Without both of these characteristics, there is little to separate air transportation from service by other modes. Indeed, many industry members promote these characteristics by offering money-back guarantees if delivery schedules are not met. Therefore, delays and cancellations have a significant and direct impact on both the air cargo industry and the shipping public that this industry serves.”  After discussions with cargo operators, a rough estimate of the value to cargo operators of avoiding weather-related flight disruptions was developed.  This benefit can be considered to be a lower bound, as it includes cargo-only operators, but leaves out the time-sensitive cargo carried on passenger flights.  This Box Value of Time benefit is estimated to add between $174M and $259M to the discounted 20-year benefit.  The distribution of this estimated benefit by airport is shown in Appendix P.

- The introduction of any new technology such as LAAS into a system as complex as the NAS may not yield benefits proportional to either the number of ground or avionics systems installed, particularly during early stages of implementation.  Due to the difficulties of providing air traffic control services to aircraft equipped with a mix of capabilities, some benefits of LAAS may not be achieved until a large proportion of the aircraft serving a particular airport are LAAS-equipped.  For example, the elimination of ILS critical areas may not be possible while a fraction of arriving aircraft still require the protection of the ILS signal for precision approach in IMC. Other LAAS capabilities, such as support of low Required Navigation Performance (RNP) procedures in the terminal area may not be as affected by this issue.  The minimum level of LAAS equipage for benefit accrual is included in the sensitivity analysis.  Results in this report may be conservative because, while LAAS benefits are subject to a minimum avionics equipage requirement, no baseline system is subject to this same requirement.

- As air traffic increases, the fraction of flights disrupted also increases.  This is particularly true for cancellations and delays, and less so for diversions. The results reported in this study are conservative because the fraction of flights disrupted is held constant for all traffic levels.

- Given the uncertainty associated with the procedures and additional technologies that will be required to support simultaneous independent parallel approaches in Cat II/III conditions in combination with LAAS, IBM chose not to quantify the potential LAAS benefits from such an application.  Any benefits that might be achievable for simultaneous independent parallel approaches in Cat II/III conditions would be in addition to those stated in this report.

- In many cases, the benefits of LAAS reported in this study are constrained by the existence of other avionics and space- or ground-based systems that may provide similar capability. However, this assumed parity does not take into account some advantages of LAAS that may prove operationally valuable, such as the ability of LAAS to improve the availability of actual navigation performance (ANP) in order to meet RNP standards, or the simplicity of using LAAS as a single system for terminal area navigation through precision approach and landing.

- Taxiway diagrams used in the ILS Critical Area benefits estimation did not explicitly indicate all existing ILS holds.  Airport and airline representatives supplied further information on critical areas at some airports.  However, the existence of unmarked critical areas at other airports may add to existing LAAS benefits.

- Current guidance from the FAA suggests that LAAS approaches will use the ILS Terminal Instrument Procedures (TERPS) surfaces.  While this may be necessary for the initial transition from ILS to LAAS-based approaches, it may also limit the benefits to be gained.  Precision approaches using TERPS surfaces designed specifically for LAAS, including missed approach procedures, may result in lower approach minima than are currently permitted when ILS-based surfaces are used.

- The methods chosen to conduct the initial computer screening of the National Transportation Safety Board (NTSB) accident records were somewhat conservative and may have missed relevant cases. The effect of potentially excluding some relevant cases is to make the associated benefit assumptions more conservative, understating the potential benefit of LAAS.

- The methodology employed in this report estimates the number of weather-related flight disruptions that would be eliminated if LAAS were to be installed at the airports studied.  In particular, this method addresses flight disruptions due to low ceiling and visibility conditions. When compared to recorded operational data from 1998–2000 this methodology estimates that LAAS would eliminate approximately 39% of the actual disruptions observed during low ceiling and visibility conditions.

- Benefits reported in the LAAS Benefits Analysis are those estimated to be possible with LAAS relative to the Navigation Capabilities Baseline documented in a November 2003 IBM report.  Some of these LAAS benefits may be reduced or eliminated if significant enhancements of the navigation system infrastructure, beyond those established in the Baseline, were to be considered.  In particular, approximately 95% of the estimated benefits are associated directly or indirectly with the ability of LAAS to provide precision guidance service.  Since this type of service can also be achieved with ILS, the installation or upgrade of ILS at all runways estimated to receive LAAS benefits would substantially reduce these benefits.  An estimated 106 to 114 new ILS installations, depending on assumed user equipage with WAAS, plus the upgrade of over 300 Cat I ILS to Cat II/III capability, will be required in order to provide benefits similar to those calculated for the 121 LAAS installations studied in this report.  Radio frequency congestion is not expected to be an issue for the studied number of LAAS installations, but may be one for ILS, particularly in some high density areas, if the number of ILS systems needed to attain these benefits are installed.  Similarly, installing the number of ILS systems required to attain these benefits may lead to an increase in the number of ILS critical areas, and an associated increase in related approach and taxi delays.

Decisions made by the FAA and the users about the preferred navigation alternative will be largely dependent on the lifecycle cost differential between installing either a single LAAS or one or more ILSs at each airport to achieve these benefits.

- Estimates of the cost of flight disruptions are central to this study.  Changes to these key cost inputs, particularly unforeseen systematic changes over time, could significantly alter these LAAS benefits estimates. IBM constructed cost estimates through extensive research, working with both government and industry sources, and has validated these estimates with airline industry representatives.  However, there is substantial uncertainty inherent in any estimate of such complex events.  For example, an FAA study shows a large range of reported costs for both diversions and cancellations, with direct operating costs of a flight diversion for jet aircraft ranging from $900 to $28,700, and the total cost of a diversion exceeding $100,000 per event.  Similarly, this FAA study, and others, have shown a large range of direct operating costs for cancellations, from $5,000 to as much as $40,000 per event.  In order to reflect this uncertainty, the cost of disruptions is included in the sensitivity analysis.

- Flight disruptions are not isolated events.  In general, a single flight disruption may have an impact on a number of other flight operations.  The extent of this impact is dependent on a number of factors, including the size, location and timing of the initial disruption, and the nature of the airline network in which it occurs.  This connection between disruptions can be accounted for by adding a factor for “downstream” effects. The specific value chosen for this factor has a substantial impact on total benefits. The estimate used here is based on a survey of published research and FAA guidance on the downstream effects of delays, the single most common form of disruption. Due to the relative importance of this factor, and the uncertainty surrounding its proper value, this report includes downstream effects in the sensitivity analysis.  Details of the treatment of downstream effects in this work are reported in Appendix N.

- Estimates of traffic increases over the 20 year period are central to this study.  While IBM has worked to ensure that the most credible and applicable estimates are used, there is substantial uncertainty in any forecast covering such a long time period.  Since the forecasts used in this work were directly based on the FAA’s 2004 Terminal Area Forecast (TAF), this study shares the forecast risks identified in the TAF documentation.  Changes to the forecasts, whether due to unforeseen economic events, world political events, or airline industry structural changes, could significantly alter the basis upon which these LAAS benefits estimates are founded.

- The primary source of approach minima (decision height and visibility) used in this work was published approaches, which supplied 77% of the minima used.  Estimates of approach minima produced by MITRE/CAASD’s GPS Approach Minima Estimator (GAME) model were used for the remaining 23% of the cases, where published approaches were not available.

- The pace of development and certification of procedures, both for LAAS and for other systems in the Baseline (particularly those with few currently existing procedures, like LPV) will be a key driver of benefits.  At the inception of this analysis, IBM and the FAA agreed to the simplifying assumption that procedures would be available within four months of each system’s IOC, on the assumption that procedure development will take place in parallel with LAAS development and implementation.  This assumption allows benefits to be calculated without the added complexity of considering procedure development schedules by airport or runway.  However, this assumption also represents a source of uncertainty in the benefits estimates in this study.

- Delay in the development and fielding of LAAS could cause significant changes to the benefit estimates.  Any delay to the assumed availability of LAAS without an associated extension to the end of the benefit study period will have a significant impact on LAAS benefit estimates.

- Changes to the assumed rate of installation of LAAS ground facilities will have a substantial impact on estimated LAAS benefits.  At the assumed rate of 24 installations per year, all 121 airports in this study can have a LAAS installed within about five years of IOC. If the actual rate of installation is reduced, then the onset of benefit accumulation will be delayed for many airports, with an associated reduction in overall benefits for the 20 year period.  See Appendix B for the schedule of LAAS installations by airport.

- The pace and extent of LAAS avionics installation among airlines will be a key driver for LAAS benefits.  In this report, IBM has assumed a certain avionics installation rate, based on feedback received from airline operations representatives.  If the actual rate is either faster or slower than assumed, benefits due to LAAS may be significantly impacted.  Similarly, if the extent of LAAS avionics equipage differs substantially from that assumed, benefits due to LAAS may be significantly impacted. In order to reflect this uncertainty, the rate of LAAS avionics equipage is included in the sensitivity analysis.

- Based on assumptions regarding IOC dates, the ground facility installation schedule, avionics equipage rates, and minimum required avionics equipage, LAAS benefits accrue at each airport over a subset of the full 20 year period. For this reason total numbers in this report cannot be divided by 20 to obtain average annual benefits per airport.

- LAAS is assumed to provide no operational improvements in some weather conditions.  See Appendix O for the list of weather types, based on National Climatic Data Center (NCDC) indicators that were eliminated from this analysis.

- Rounding of estimated LAAS benefits leads to some minor discrepancies between tabulated values.  For example, Table 4A ABQ Total Benefit is $2.375 million versus Table J1 ABQ Total Benefit is $2.374 million.

- The types of events that were considered in the Safety analysis are relatively rare events. Consequently, even one additional air carrier crash event could have a profound effect on the resulting accident rates and future benefit projections. This problem does not invalidate the results, but needs to be considered since these events are rare.

- IBM has investigated the potential quantitative LAAS Societal benefits that may be obtained through (1) sales of LAAS Ground Facility (LGF) and LAAS avionics to international airports and airlines, and (2) increased U.S. Airport Improvement Program and U.S airline revenue to demonstrate the impact of a hypothetical 1% increased load factor on 1% of operations.  These quantitative societal benefits are speculative, and are included only to illustrate the importance of the economic impact that LAAS may provide.  These benefits estimates are not incorporated into the total benefits derived from either the efficiency or safety benefits analyses.

It is possible that many of the potential LAAS Societal benefits may also be achieved through current or emerging procedures (e.g., RNAV/RNP) or technologies (e.g., WAAS).

# General Approach

## Incremental Benefits

The diagram below illustrates the general approach used to estimate the incremental benefits expected from LAAS.  The first step in this process was to determine the current and planned capabilities of existing and expected navigation systems (collectively known as the Navigation Capabilities Baseline) during the 20 year time horizon (from 2009 to 2028).  The capabilities were those assumed to be available from the ground and space-based infrastructure in conjunction with airborne avionics.  The second step was to identify the capabilities provided by LAAS during the same time frame.  The LAAS incremental capabilities resulted from an analysis of the differences between the capabilities of systems in the baseline and the capabilities of LAAS.  The third and final step was to quantify (in monetary terms), based on actual and forecasted operational data, the LAAS incremental benefits derived from these capability differences.

## Scope and Key Assumptions

The LAAS benefits analysis focuses on the cost savings that can be achieved by the likely users of LAAS navigation technology during the 20 year period from 2009 to 2028 at 121 airports.  These users are the major passenger airlines, major cargo airlines, regional airlines, corporate/business operators, and the operators of small general aviation aircraft in Alaska who may have special needs for such equipment because of the unique challenges of flying in Alaska.  The 121 airports were selected from the relatively high-volume commercial and business airports that are currently being utilized by potential LAAS users, the 6 Low Rate Initial Production (LRIP) sites, the 35 Operational Evolution Plan (OEP) airports, and the airports that either currently have or are qualified to receive Cat II/III ILSs (see Appendix A).

Based on the latest guidance from the FAA, IBM assumed that the LAAS Cat I and Cat II/III would have Initial Operational Capability (IOC) dates of 2009 and 2013, respectively.  In addition various assumptions had to be made about the ground and avionics installation and procedure availability schedules.  A few of the key assumptions included the following:

- Ground facilities will be installed in the order of total airport benefits

- The users will take approximately 6 years to equip their fleets with LAAS avionics

- Benefits will not be attained until a required equipage level of 80% in avionics equipage is achieved

- Procedure development will proceed in parallel with LAAS installations and procedures will be available 4 months after installation at each site to allow for flight checks

Since the avionics equipage schedule and the minimum required equipage level assumptions are uncertain, IBM conducted sensitivity analyses to determine the effects on the analysis results of variation in these values.  In addition, IBM considered two scenarios related to users’ Wide Area Augmentation System (WAAS) equipage levels – 0% and 100% equipage were evaluated in order to bound the potential effects of WAAS on LAAS benefits.

In addition, a multiplicative factor was applied to the results to reflect the downstream effects typically encountered with flight disruptions.  Finally, since the outcome of this analysis is stated in terms of the dollar savings in direct operating costs and passenger time, a discount rate was applied to convert future dollar values to 2004 dollars.  The rate that was selected by IBM was a 7% real discount rate, as recommended by the Office of Management and Budget (OMB)  for such analyses.

## Validation of  Methodology and Data

An important activity throughout this study was the validation of both the methodology and specific key inputs with a wide range of service provider and airline industry representatives (see Appendix Q).  Feedback was obtained from written comments provided by reviewers, from meetings with principal airport and airline groups, and from site visits to five key airports and airlines.  The purpose of these meetings and site visits was to communicate IBM’s methodologies and preliminary findings, to gain a better understanding of current and expected airline and air traffic operations from a variety of viewpoints, and to explore how LAAS may provide additional benefit to such operations.

Data gathered during these visits was used to either validate or correct the methodology, the mathematical formulas, and the specific critical inputs that IBM used to quantify the incremental benefits of LAAS.

# Efficiency Benefits

## Summary of Efficiency Benefits

Table 2A shows the best estimate for the total 20 year discounted efficiency benefits estimated for all 121 airports.  Tables 2B and 2C show the 5th and 95th percentiles, respectively.  The percentiles are obtained through the sensitivity analysis which evaluates the impact on benefits of the variability in several key input parameters, including the cost of disruptions, the pace of LAAS equipage, the minimum required equipage for benefit accrual, the average length of a delay, and the ripple effect of delays. See Appendix D for details of the sensitivity analysis. Further tables in this paper report best estimate values.

Benefits are shown for both reduced direct operating costs (DOC) and passenger time savings (PTS).  These are reported separately here and in subsequent tables so that readers can easily distinguish the magnitude of benefits accruing to these two distinct groups.

User decisions regarding WAAS avionics equipage are a key element in estimating LAAS benefits.  In order to place bounds on this element, IBM and the FAA agreed that LAAS benefits in this report shall be stated for two extreme cases: no WAAS equipage by any users, and full WAAS equipage by all users.  While neither of these two cases is likely to be realistic, together they provide an upper and lower bound for LAAS benefits relative to WAAS equipage.  Thus, in Tables 2A, B, and C and subsequent tables in this paper, LAAS benefits are shown for the two alternative cases of user equipage with WAAS: assuming no WAAS equipage by users (“0% WAAS”), and assuming full WAAS equipage by users (“100% WAAS”).

Table 2a: Discounted 20 year LAAS Efficiency Benefits – Best Estimate

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $638,900,000 | $795,80,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $429,300,000 | $542,100,000 |

Table 2b: Discounted 20 year LAAS Efficiency Benefits – 5th Percentile

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $623,900,000 | $735,100,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $409,700,000 | $479,800,000 |

Table 2c: Discounted 20 year LAAS Efficiency Benefits – 95th Percentile

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $786,700,000 | $923,200,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $543,300,000 | $620,200,000 |

Tables 3A and 3B show the total 20 year discounted efficiency benefits by user group. Table 3A lists direct operating cost benefits, and Table 3B lists passenger time savings.  Further details of benefits by user group, listed by airport, are in Appendix J.

### Benefits by User Group

Table 3a: Discounted 20 year LAAS Operating Cost Efficiency Benefits – by User Group

|  | Major Passenger Airlines | Regional Passenger Airlines | Cargo Carriers | Corporate Jet GA Operators | Other GA Operators |
| --- | --- | --- | --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $434,900,000 | $128,000,000 | $39,800,000 | $26,700,000 | $9,500,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $296,000,000 | $86,600,000 | $26,500,000 | $19,500,000 | $700,000 |

Table 3b: Discounted 20 year LAAS Passenger Time Savings Efficiency Benefits – by User Group

|  | Major Passenger Airlines | Regional Passenger Airlines | Cargo Carriers | Corporate Jet GA Operators | Other GA Operators |
| --- | --- | --- | --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $578,600,000 | $209,000,000 | $0 | $5,400,000 | $2,800,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $396,000,000 | $141,800,000 | $0 | $4,100,000 | $200,000 |

### Benefits by Efficiency Benefit Categories and by Airport

The LAAS efficiency benefits estimated in this report are attributable to each of the five quantified efficiency benefit categories:

- Straight-in Approaches

- Takeoff Guidance

- Complex Procedures

- ILS Critical Area Elimination

- Closely Spaced Simultaneous Independent Parallel Approaches

The pie charts in Figure 1 show the portion of the benefits attributable to each of the five quantified efficiency benefit categories, as summarized in Table 2A.  Tables 4A and B and 5A and B list these benefits for each of the121 airports.

Figure 1. proportion of the Discounted 20 year LAAS Estimated Benefits Attributable to each of the Five Quantified Efficiency Benefit Categories

### Estimated LAAS Benefits Assuming No User Equipage with WAAS

Tables 4A and 4B show the 20 year discounted efficiency benefits, by airport, for the scenario in which users do not equip with WAAS.  These values provide the upper bound of estimated LAAS benefits relative to WAAS equipage by users.  User operating cost benefits are shown in Table 4A, and passenger time cost savings are shown in Table 4B.  Each airport’s rank in terms of total benefit is shown in the third column.  In addition to total benefit at each airport, the contribution to the total from each separate efficiency benefit category is shown.

Table 4a: Discounted 20 Year LAAS Operating Cost Benefits – 0% WAAS Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Straight-In Approach | Takeoff Guidance | Complex Approach | ILS Critical Area | Parallel Approach |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $2,375,000 | 73 | $2,136,000 | $239,000 | $0 | $0 | $0 |
| ACK | $7,638,000 | 28 | $7,638,000 | $0 | $0 | $0 | $0 |
| AFW | $149,000 | 116 | $148,000 | $1,000 | $0 | $0 | $0 |
| ALB | $8,501,000 | 24 | $3,298,000 | $1,088,000 | $4,115,000 | $0 | $0 |
| ANC | $8,320,000 | 25 | $8,298,000 | $22,000 | $0 | $0 | $0 |
| ATL | $13,199,000 | 11 | $9,826,000 | $0 | $0 | $3,373,000 | $0 |
| AUS | $3,149,000 | 59 | $2,957,000 | $192,000 | $0 | $0 | $0 |
| AVL | $738,000 | 95 | $363,000 | $375,000 | $0 | $0 | $0 |
| BDL | $10,190,000 | 18 | $2,270,000 | $90,000 | $7,830,000 | $0 | $0 |
| BFI | $540,000 | 101 | $225,000 | $315,000 | $0 | $0 | $0 |
| BGR | $344,000 | 109 | $330,000 | $14,000 | $0 | $0 | $0 |
| BHM | $6,020,000 | 34 | $873,000 | $0 | $5,147,000 | $0 | $0 |
| BNA | $2,194,000 | 76 | $2,194,000 | $0 | $0 | $0 | $0 |
| BOI | $2,521,000 | 70 | $2,521,000 | $0 | $0 | $0 | $0 |
| BOS | $10,484,000 | 17 | $10,484,000 | $0 | $0 | $0 | $0 |
| BUF | $4,828,000 | 45 | $4,805,000 | $23,000 | $0 | $0 | $0 |
| BUR | $20,775,000 | 7 | $4,963,000 | $272,000 | $15,540,000 | $0 | $0 |
| BWI | $5,106,000 | 42 | $5,106,000 | $0 | $0 | $0 | $0 |
| CAE | $1,645,000 | 80 | $1,643,000 | $2,000 | $0 | $0 | $0 |
| CHA | $309,000 | 111 | $309,000 | $0 | $0 | $0 | $0 |
| CHS | $2,243,000 | 75 | $2,243,000 | $0 | $0 | $0 | $0 |
| CLE | $21,215,000 | 5 | $21,215,000 | $0 | $0 | $0 | $0 |
| CLT | $11,320,000 | 15 | $11,320,000 | $0 | $0 | $0 | $0 |
| CMH | $3,292,000 | 58 | $2,697,000 | $595,000 | $0 | $0 | $0 |
| COS | $6,250,000 | 32 | $4,600,000 | $1,650,000 | $0 | $0 | $0 |
| CVG | $13,033,000 | 12 | $7,417,000 | $0 | $0 | $5,616,000 | $0 |
| DAB | $462,000 | 104 | $222,000 | $240,000 | $0 | $0 | $0 |
| DAL | $2,960,000 | 63 | $1,496,000 | $1,464,000 | $0 | $0 | $0 |
| DAY | $2,436,000 | 71 | $2,360,000 | $1,000 | $0 | $75,000 | $0 |
| DCA | $27,535,000 | 3 | $1,927,000 | $0 | $25,608,000 | $0 | $0 |
| DEN | $14,829,000 | 10 | $14,829,000 | $0 | $0 | $0 | $0 |
| DFW | $34,071,000 | 1 | $16,127,000 | $0 | $0 | $17,944,000 | $0 |
| DLH | $532,000 | 102 | $284,000 | $248,000 | $0 | $0 | $0 |
| DSM | $1,227,000 | 86 | $1,227,000 | $0 | $0 | $0 | $0 |
| DTW | $29,189,000 | 2 | $23,309,000 | $0 | $0 | $2,461,000 | $3,419,000 |
| DVT | $4,000 | 121 | $4,000 | $0 | $0 | $0 | $0 |
| ELP | $84,000 | 118 | $57,000 | $27,000 | $0 | $0 | $0 |
| EUG | $2,595,000 | 67 | $1,532,000 | $1,063,000 | $0 | $0 | $0 |
| EWR | $9,749,000 | 20 | $9,749,000 | $0 | $0 | $0 | $0 |
| EYW | $280,000 | 113 | $279,000 | $1,000 | $0 | $0 | $0 |
| FAI | $715,000 | 96 | $715,000 | $0 | $0 | $0 | $0 |
| FAT | $301,000 | 112 | $269,000 | $32,000 | $0 | $0 | $0 |
| FLL | $2,680,000 | 65 | $2,196,000 | $289,000 | $0 | $0 | $195,000 |
| FWA | $2,545,000 | 69 | $2,507,000 | $38,000 | $0 | $0 | $0 |
| FXE | $45,000 | 120 | $34,000 | $11,000 | $0 | $0 | $0 |
| GEG | $5,372,000 | 39 | $5,298,000 | $74,000 | $0 | $0 | $0 |
| GRR | $3,870,000 | 53 | $2,928,000 | $942,000 | $0 | $0 | $0 |
| GSO | $4,796,000 | 46 | $4,796,000 | $0 | $0 | $0 | $0 |
| GSP | $850,000 | 94 | $850,000 | $0 | $0 | $0 | $0 |
| HNL | $2,667,000 | 66 | $86,000 | $0 | $2,581,000 | $0 | $0 |
| HOU | $9,799,000 | 19 | $4,992,000 | $4,807,000 | $0 | $0 | $0 |
| HPN | $6,460,000 | 31 | $2,328,000 | $3,947,000 | $0 | $185,000 | $0 |
| HSV | $551,000 | 100 | $255,000 | $296,000 | $0 | $0 | $0 |
| IAD | $7,093,000 | 29 | $7,093,000 | $0 | $0 | $0 | $0 |
| IAH | $10,988,000 | 16 | $9,879,000 | $0 | $0 | $1,109,000 | $0 |
| ICT | $1,874,000 | 78 | $1,874,000 | $0 | $0 | $0 | $0 |
| ILN | $1,046,000 | 90 | $1,045,000 | $1,000 | $0 | $0 | $0 |
| IND | $2,834,000 | 64 | $2,834,000 | $0 | $0 | $0 | $0 |
| ISP | $4,097,000 | 50 | $3,226,000 | $871,000 | $0 | $0 | $0 |
| JAN | $336,000 | 110 | $333,000 | $3,000 | $0 | $0 | $0 |
| JAX | $1,778,000 | 79 | $1,773,000 | $5,000 | $0 | $0 | $0 |
| JFK | $4,527,000 | 49 | $4,268,000 | $0 | $0 | $0 | $259,000 |
| JNU | $13,022,000 | 13 | $0 | $103,000 | $12,919,000 | $0 | $0 |
| LAS | $406,000 | 106 | $402,000 | $4,000 | $0 | $0 | $0 |
| LAX | $6,752,000 | 30 | $6,752,000 | $0 | $0 | $0 | $0 |
| LCK | $137,000 | 117 | $79,000 | $58,000 | $0 | $0 | $0 |
| LGA | $20,987,000 | 6 | $12,296,000 | $0 | $8,691,000 | $0 | $0 |
| LGB | $5,320,000 | 41 | $1,787,000 | $1,589,000 | $0 | $0 | $1,944,000 |
| LIT | $691,000 | 97 | $594,000 | $97,000 | $0 | $0 | $0 |
| MCI | $4,000,000 | 51 | $4,000,000 | $0 | $0 | $0 | $0 |
| MCO | $4,723,000 | 48 | $3,975,000 | $0 | $0 | $748,000 | $0 |
| MDT | $1,464,000 | 85 | $1,063,000 | $401,000 | $0 | $0 | $0 |
| MDW | $16,085,000 | 9 | $13,766,000 | $2,319,000 | $0 | $0 | $0 |
| MEM | $8,906,000 | 23 | $6,331,000 | $0 | $0 | $313,000 | $2,262,000 |
| MHT | $7,929,000 | 27 | $7,202,000 | $727,000 | $0 | $0 | $0 |
| MIA | $4,985,000 | 44 | $4,985,000 | $0 | $0 | $0 | $0 |
| MKE | $12,903,000 | 14 | $12,549,000 | $6,000 | $0 | $204,000 | $144,000 |
| MMU | $406,000 | 107 | $237,000 | $169,000 | $0 | $0 | $0 |
| MSP | $6,041,000 | 33 | $6,041,000 | $0 | $0 | $0 | $0 |
| MSY | $5,091,000 | 43 | $4,921,000 | $170,000 | $0 | $0 | $0 |
| OAK | $1,188,000 | 88 | $899,000 | $289,000 | $0 | $0 | $0 |
| OKC | $3,859,000 | 54 | $3,751,000 | $108,000 | $0 | $0 | $0 |
| OMA | $1,115,000 | 89 | $1,115,000 | $0 | $0 | $0 | $0 |
| ONT | $364,000 | 108 | $364,000 | $0 | $0 | $0 | $0 |
| ORD | $23,601,000 | 4 | $23,039,000 | $0 | $0 | $562,000 | $0 |
| ORF | $4,754,000 | 47 | $3,614,000 | $1,064,000 | $0 | $76,000 | $0 |
| PBI | $1,547,000 | 84 | $1,402,000 | $145,000 | $0 | $0 | $0 |
| PDX | $3,080,000 | 61 | $2,735,000 | $294,000 | $0 | $0 | $51,000 |
| PHL | $5,772,000 | 35 | $5,145,000 | $0 | $0 | $627,000 | $0 |
| PHX | $3,082,000 | 60 | $1,375,000 | $1,707,000 | $0 | $0 | $0 |
| PIE | $501,000 | 103 | $314,000 | $187,000 | $0 | $0 | $0 |
| PIT | $8,132,000 | 26 | $8,132,000 | $0 | $0 | $0 | $0 |
| PVD | $5,379,000 | 38 | $3,444,000 | $1,935,000 | $0 | $0 | $0 |
| RDU | $3,931,000 | 52 | $3,868,000 | $2,000 | $0 | $0 | $61,000 |
| RFD | $1,560,000 | 83 | $966,000 | $594,000 | $0 | $0 | $0 |
| RIC | $5,526,000 | 37 | $5,394,000 | $91,000 | $0 | $41,000 | $0 |
| RNO | $2,421,000 | 72 | $2,347,000 | $74,000 | $0 | $0 | $0 |
| ROC | $1,633,000 | 81 | $791,000 | $9,000 | $0 | $833,000 | $0 |
| RSW | $5,610,000 | 36 | $2,915,000 | $2,695,000 | $0 | $0 | $0 |
| SAN | $16,784,000 | 8 | $0 | $0 | $16,784,000 | $0 | $0 |
| SAT | $2,074,000 | 77 | $1,895,000 | $179,000 | $0 | $0 | $0 |
| SDF | $560,000 | 99 | $560,000 | $0 | $0 | $0 | $0 |
| SEA | $9,276,000 | 21 | $7,304,000 | $0 | $0 | $1,972,000 | $0 |
| SFB | $179,000 | 115 | $106,000 | $73,000 | $0 | $0 | $0 |
| SFO | $2,253,000 | 74 | $2,225,000 | $28,000 | $0 | $0 | $0 |
| SHV | $890,000 | 93 | $890,000 | $0 | $0 | $0 | $0 |
| SJC | $9,198,000 | 22 | $7,039,000 | $2,159,000 | $0 | $0 | $0 |
| SLC | $5,345,000 | 40 | $3,783,000 | $0 | $0 | $0 | $1,562,000 |
| SMF | $2,974,000 | 62 | $2,674,000 | $300,000 | $0 | $0 | $0 |
| SNA | $3,459,000 | 56 | $209,000 | $3,250,000 | $0 | $0 | $0 |
| STL | $2,580,000 | 68 | $2,576,000 | $4,000 | $0 | $0 | $0 |
| SWF | $460,000 | 105 | $443,000 | $17,000 | $0 | $0 | $0 |
| SYR | $1,195,000 | 87 | $1,193,000 | $2,000 | $0 | $0 | $0 |
| TEB | $3,464,000 | 55 | $420,000 | $803,000 | $2,241,000 | $0 | $0 |
| TLH | $1,622,000 | 82 | $902,000 | $720,000 | $0 | $0 | $0 |
| TPA | $3,339,000 | 57 | $1,973,000 | $1,366,000 | $0 | $0 | $0 |
| TRI | $272,000 | 114 | $272,000 | $0 | $0 | $0 | $0 |
| TUL | $984,000 | 91 | $984,000 | $0 | $0 | $0 | $0 |
| TUS | $63,000 | 119 | $55,000 | $8,000 | $0 | $0 | $0 |
| TYS | $902,000 | 92 | $901,000 | $1,000 | $0 | $0 | $0 |
| VNY | $568,000 | 98 | $390,000 | $178,000 | $0 | $0 | $0 |
| Total | $638,899,000 |  | $448,244,000 | $43,163,000 | $101,456,000 | $36,139,000 | $9,897,000 |

Table 4b: Discounted 20 Year LAAS Passenger Time Savings – 0% WAAS Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Straight-In Approach | Takeoff Guidance | Complex Approach | ILS Critical Area | Parallel Approach |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $2,946,000 | 69 | $2,625,000 | $321,000 | $0 | $0 | $0 |
| ACK | $11,478,000 | 22 | $11,478,000 | $0 | $0 | $0 | $0 |
| AFW | $2,000 | 118 | $2,000 | $0 | $0 | $0 | $0 |
| ALB | $11,300,000 | 23 | $4,407,000 | $1,418,000 | $5,475,000 | $0 | $0 |
| ANC | $5,384,000 | 49 | $5,372,000 | $12,000 | $0 | $0 | $0 |
| ATL | $18,415,000 | 11 | $12,793,000 | $0 | $0 | $5,622,000 | $0 |
| AUS | $3,959,000 | 59 | $3,682,000 | $277,000 | $0 | $0 | $0 |
| AVL | $886,000 | 92 | $510,000 | $376,000 | $0 | $0 | $0 |
| BDL | $12,215,000 | 19 | $2,716,000 | $106,000 | $9,393,000 | $0 | $0 |
| BFI | $107,000 | 113 | $49,000 | $58,000 | $0 | $0 | $0 |
| BGR | $445,000 | 101 | $436,000 | $9,000 | $0 | $0 | $0 |
| BHM | $7,220,000 | 34 | $1,082,000 | $0 | $6,138,000 | $0 | $0 |
| BNA | $2,777,000 | 72 | $2,777,000 | $0 | $0 | $0 | $0 |
| BOI | $3,194,000 | 65 | $3,194,000 | $0 | $0 | $0 | $0 |
| BOS | $14,053,000 | 16 | $14,053,000 | $0 | $0 | $0 | $0 |
| BUF | $6,196,000 | 40 | $6,164,000 | $32,000 | $0 | $0 | $0 |
| BUR | $26,027,000 | 7 | $6,213,000 | $392,000 | $19,422,000 | $0 | $0 |
| BWI | $6,470,000 | 36 | $6,470,000 | $0 | $0 | $0 | $0 |
| CAE | $1,806,000 | 81 | $1,805,000 | $1,000 | $0 | $0 | $0 |
| CHA | $348,000 | 107 | $348,000 | $0 | $0 | $0 | $0 |
| CHS | $3,023,000 | 67 | $3,023,000 | $0 | $0 | $0 | $0 |
| CLE | $28,585,000 | 5 | $28,585,000 | $0 | $0 | $0 | $0 |
| CLT | $14,739,000 | 14 | $14,739,000 | $0 | $0 | $0 | $0 |
| CMH | $4,309,000 | 57 | $3,564,000 | $745,000 | $0 | $0 | $0 |
| COS | $8,037,000 | 29 | $5,810,000 | $2,227,000 | $0 | $0 | $0 |
| CVG | $15,890,000 | 13 | $9,997,000 | $0 | $0 | $5,893,000 | $0 |
| DAB | $450,000 | 100 | $254,000 | $196,000 | $0 | $0 | $0 |
| DAL | $3,124,000 | 66 | $1,697,000 | $1,427,000 | $0 | $0 | $0 |
| DAY | $2,605,000 | 74 | $2,525,000 | $1,000 | $0 | $79,000 | $0 |
| DCA | $36,752,000 | 3 | $2,615,000 | $0 | $34,137,000 | $0 | $0 |
| DEN | $19,332,000 | 10 | $19,332,000 | $0 | $0 | $0 | $0 |
| DFW | $49,928,000 | 1 | $21,097,000 | $0 | $0 | $28,831,000 | $0 |
| DLH | $513,000 | 99 | $323,000 | $190,000 | $0 | $0 | $0 |
| DSM | $1,392,000 | 85 | $1,392,000 | $0 | $0 | $0 | $0 |
| DTW | $39,393,000 | 2 | $31,175,000 | $0 | $0 | $4,091,000 | $4,127,000 |
| DVT | $1,000 | 119 | $1,000 | $0 | $0 | $0 | $0 |
| ELP | $101,000 | 114 | $71,000 | $30,000 | $0 | $0 | $0 |
| EUG | $2,968,000 | 68 | $2,044,000 | $924,000 | $0 | $0 | $0 |
| EWR | $12,052,000 | 20 | $12,052,000 | $0 | $0 | $0 | $0 |
| EYW | $436,000 | 102 | $435,000 | $1,000 | $0 | $0 | $0 |
| FAI | $535,000 | 97 | $535,000 | $0 | $0 | $0 | $0 |
| FAT | $429,000 | 103 | $399,000 | $30,000 | $0 | $0 | $0 |
| FLL | $3,477,000 | 63 | $2,854,000 | $408,000 | $0 | $0 | $215,000 |
| FWA | $2,715,000 | 73 | $2,702,000 | $13,000 | $0 | $0 | $0 |
| FXE | $9,000 | 117 | $6,000 | $3,000 | $0 | $0 | $0 |
| GEG | $6,044,000 | 42 | $5,972,000 | $72,000 | $0 | $0 | $0 |
| GRR | $4,044,000 | 58 | $3,268,000 | $776,000 | $0 | $0 | $0 |
| GSO | $5,751,000 | 45 | $5,751,000 | $0 | $0 | $0 | $0 |
| GSP | $1,162,000 | 90 | $1,162,000 | $0 | $0 | $0 | $0 |
| HNL | $3,834,000 | 61 | $135,000 | $0 | $3,699,000 | $0 | $0 |
| HOU | $12,575,000 | 17 | $6,166,000 | $6,409,000 | $0 | $0 | $0 |
| HPN | $5,460,000 | 48 | $2,734,000 | $2,511,000 | $0 | $215,000 | $0 |
| HSV | $563,000 | 96 | $306,000 | $257,000 | $0 | $0 | $0 |
| IAD | $9,718,000 | 25 | $9,718,000 | $0 | $0 | $0 | $0 |
| IAH | $14,353,000 | 15 | $13,006,000 | $0 | $0 | $1,347,000 | $0 |
| ICT | $1,899,000 | 79 | $1,899,000 | $0 | $0 | $0 | $0 |
| ILN | $0 | 120 | $0 | $0 | $0 | $0 | $0 |
| IND | $2,393,000 | 75 | $2,393,000 | $0 | $0 | $0 | $0 |
| ISP | $5,973,000 | 43 | $4,603,000 | $1,370,000 | $0 | $0 | $0 |
| JAN | $395,000 | 105 | $392,000 | $3,000 | $0 | $0 | $0 |
| JAX | $2,160,000 | 77 | $2,154,000 | $6,000 | $0 | $0 | $0 |
| JFK | $5,556,000 | 47 | $5,250,000 | $0 | $0 | $0 | $306,000 |
| JNU | $5,670,000 | 46 | $0 | $101,000 | $5,569,000 | $0 | $0 |
| LAS | $515,000 | 98 | $509,000 | $6,000 | $0 | $0 | $0 |
| LAX | $8,693,000 | 27 | $8,693,000 | $0 | $0 | $0 | $0 |
| LCK | $0 | 121 | $0 | $0 | $0 | $0 | $0 |
| LGA | $28,334,000 | 6 | $16,601,000 | $0 | $11,733,000 | $0 | $0 |
| LGB | $4,578,000 | 55 | $1,722,000 | $1,320,000 | $0 | $0 | $1,536,000 |
| LIT | $740,000 | 93 | $648,000 | $92,000 | $0 | $0 | $0 |
| MCI | $5,096,000 | 51 | $5,096,000 | $0 | $0 | $0 | $0 |
| MCO | $6,415,000 | 38 | $5,265,000 | $0 | $0 | $1,150,000 | $0 |
| MDT | $1,665,000 | 83 | $1,284,000 | $381,000 | $0 | $0 | $0 |
| MDW | $22,048,000 | 8 | $18,093,000 | $3,955,000 | $0 | $0 | $0 |
| MEM | $8,144,000 | 28 | $5,445,000 | $0 | $0 | $250,000 | $2,449,000 |
| MHT | $9,579,000 | 26 | $8,671,000 | $908,000 | $0 | $0 | $0 |
| MIA | $5,920,000 | 44 | $5,920,000 | $0 | $0 | $0 | $0 |
| MKE | $17,123,000 | 12 | $16,716,000 | $6,000 | $0 | $274,000 | $127,000 |
| MMU | $83,000 | 115 | $42,000 | $41,000 | $0 | $0 | $0 |
| MSP | $7,927,000 | 30 | $7,927,000 | $0 | $0 | $0 | $0 |
| MSY | $6,352,000 | 39 | $6,101,000 | $251,000 | $0 | $0 | $0 |
| OAK | $1,194,000 | 89 | $859,000 | $335,000 | $0 | $0 | $0 |
| OKC | $4,660,000 | 54 | $4,537,000 | $123,000 | $0 | $0 | $0 |
| OMA | $1,222,000 | 86 | $1,222,000 | $0 | $0 | $0 | $0 |
| ONT | $399,000 | 104 | $399,000 | $0 | $0 | $0 | $0 |
| ORD | $30,997,000 | 4 | $30,070,000 | $0 | $0 | $927,000 | $0 |
| ORF | $6,173,000 | 41 | $4,708,000 | $1,388,000 | $0 | $77,000 | $0 |
| PBI | $1,879,000 | 80 | $1,742,000 | $137,000 | $0 | $0 | $0 |
| PDX | $3,911,000 | 60 | $3,469,000 | $386,000 | $0 | $0 | $56,000 |
| PHL | $7,398,000 | 33 | $6,452,000 | $0 | $0 | $946,000 | $0 |
| PHX | $4,441,000 | 56 | $1,787,000 | $2,654,000 | $0 | $0 | $0 |
| PIE | $264,000 | 109 | $189,000 | $75,000 | $0 | $0 | $0 |
| PIT | $10,901,000 | 24 | $10,901,000 | $0 | $0 | $0 | $0 |
| PVD | $7,614,000 | 32 | $4,777,000 | $2,837,000 | $0 | $0 | $0 |
| RDU | $5,302,000 | 50 | $5,243,000 | $3,000 | $0 | $0 | $56,000 |
| RFD | $163,000 | 110 | $122,000 | $41,000 | $0 | $0 | $0 |
| RIC | $6,786,000 | 35 | $6,646,000 | $102,000 | $0 | $38,000 | $0 |
| RNO | $2,911,000 | 70 | $2,816,000 | $95,000 | $0 | $0 | $0 |
| ROC | $2,026,000 | 78 | $922,000 | $10,000 | $0 | $1,094,000 | $0 |
| RSW | $7,757,000 | 31 | $3,781,000 | $3,976,000 | $0 | $0 | $0 |
| SAN | $21,360,000 | 9 | $0 | $0 | $21,360,000 | $0 | $0 |
| SAT | $2,331,000 | 76 | $2,133,000 | $198,000 | $0 | $0 | $0 |
| SDF | $387,000 | 106 | $387,000 | $0 | $0 | $0 | $0 |
| SEA | $12,268,000 | 18 | $9,536,000 | $0 | $0 | $2,732,000 | $0 |
| SFB | $154,000 | 111 | $121,000 | $33,000 | $0 | $0 | $0 |
| SFO | $2,908,000 | 71 | $2,863,000 | $45,000 | $0 | $0 | $0 |
| SHV | $1,213,000 | 88 | $1,213,000 | $0 | $0 | $0 | $0 |
| SJC | $11,881,000 | 21 | $8,654,000 | $3,227,000 | $0 | $0 | $0 |
| SLC | $6,426,000 | 37 | $4,693,000 | $0 | $0 | $0 | $1,733,000 |
| SMF | $3,651,000 | 62 | $3,238,000 | $413,000 | $0 | $0 | $0 |
| SNA | $4,759,000 | 52 | $115,000 | $4,644,000 | $0 | $0 | $0 |
| STL | $3,407,000 | 64 | $3,400,000 | $7,000 | $0 | $0 | $0 |
| SWF | $670,000 | 94 | $659,000 | $11,000 | $0 | $0 | $0 |
| SYR | $1,571,000 | 84 | $1,569,000 | $2,000 | $0 | $0 | $0 |
| TEB | $652,000 | 95 | $72,000 | $192,000 | $388,000 | $0 | $0 |
| TLH | $1,799,000 | 82 | $1,225,000 | $574,000 | $0 | $0 | $0 |
| TPA | $4,707,000 | 53 | $2,611,000 | $2,096,000 | $0 | $0 | $0 |
| TRI | $347,000 | 108 | $347,000 | $0 | $0 | $0 | $0 |
| TUL | $1,222,000 | 87 | $1,222,000 | $0 | $0 | $0 | $0 |
| TUS | $77,000 | 116 | $68,000 | $9,000 | $0 | $0 | $0 |
| TYS | $1,097,000 | 91 | $1,096,000 | $1,000 | $0 | $0 | $0 |
| VNY | $113,000 | 112 | $70,000 | $43,000 | $0 | $0 | $0 |
| Total | $795,783,000 |  | $562,979,000 | $51,319,000 | $117,314,000 | $53,566,000 | $10,605,000 |

### Estimated LAAS Benefits Assuming Full User Equipage with WAAS

Tables 5A and 5B show the 20 year discounted efficiency benefits, by airport, for the scenario in which users equip with WAAS.   These values provide the lower bound of estimated LAAS benefits relative to WAAS equipage by users.  User operating cost benefits are shown in Table 5A, and passenger time cost savings are shown in Table 5B.  Each airport’s rank in terms of total benefit is shown in the third column.  In addition to total benefit at each airport, the contribution to the total from each separate efficiency benefit category is shown.

Table 5a: Discounted 20 Year LAAS Operating Cost Benefits – 0% WAAS Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Straight-In Approach | Takeoff Guidance | Complex Approach | ILS Critical Area | Parallel Approach |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $1,132,000 | 74 | $893,000 | $239,000 | $0 | $0 | $0 |
| ACK | $7,638,000 | 16 | $7,638,000 | $0 | $0 | $0 | $0 |
| AFW | $149,000 | 112 | $148,000 | $1,000 | $0 | $0 | $0 |
| ALB | $5,381,000 | 25 | $3,298,000 | $1,088,000 | $995,000 | $0 | $0 |
| ANC | $4,619,000 | 33 | $4,597,000 | $22,000 | $0 | $0 | $0 |
| ATL | $11,923,000 | 7 | $9,826,000 | $0 | $0 | $2,097,000 | $0 |
| AUS | $3,149,000 | 46 | $2,957,000 | $192,000 | $0 | $0 | $0 |
| AVL | $738,000 | 86 | $363,000 | $375,000 | $0 | $0 | $0 |
| BDL | $3,509,000 | 42 | $2,270,000 | $90,000 | $1,149,000 | $0 | $0 |
| BFI | $540,000 | 94 | $225,000 | $315,000 | $0 | $0 | $0 |
| BGR | $344,000 | 103 | $330,000 | $14,000 | $0 | $0 | $0 |
| BHM | $386,000 | 100 | $196,000 | $0 | $190,000 | $0 | $0 |
| BNA | $1,142,000 | 73 | $1,142,000 | $0 | $0 | $0 | $0 |
| BOI | $2,521,000 | 59 | $2,521,000 | $0 | $0 | $0 | $0 |
| BOS | $10,484,000 | 10 | $10,484,000 | $0 | $0 | $0 | $0 |
| BUF | $4,517,000 | 34 | $4,494,000 | $23,000 | $0 | $0 | $0 |
| BUR | $585,000 | 90 | $56,000 | $272,000 | $257,000 | $0 | $0 |
| BWI | $5,106,000 | 26 | $5,106,000 | $0 | $0 | $0 | $0 |
| CAE | $1,021,000 | 79 | $1,019,000 | $2,000 | $0 | $0 | $0 |
| CHA | $290,000 | 108 | $290,000 | $0 | $0 | $0 | $0 |
| CHS | $1,274,000 | 70 | $1,274,000 | $0 | $0 | $0 | $0 |
| CLE | $4,949,000 | 29 | $4,949,000 | $0 | $0 | $0 | $0 |
| CLT | $11,320,000 | 8 | $11,320,000 | $0 | $0 | $0 | $0 |
| CMH | $3,292,000 | 45 | $2,697,000 | $595,000 | $0 | $0 | $0 |
| COS | $4,999,000 | 28 | $3,349,000 | $1,650,000 | $0 | $0 | $0 |
| CVG | $9,628,000 | 12 | $7,417,000 | $0 | $0 | $2,211,000 | $0 |
| DAB | $462,000 | 98 | $222,000 | $240,000 | $0 | $0 | $0 |
| DAL | $2,960,000 | 53 | $1,496,000 | $1,464,000 | $0 | $0 | $0 |
| DAY | $1,307,000 | 69 | $1,231,000 | $1,000 | $0 | $75,000 | $0 |
| DCA | $2,763,000 | 56 | $1,749,000 | $0 | $1,014,000 | $0 | $0 |
| DEN | $14,829,000 | 4 | $14,829,000 | $0 | $0 | $0 | $0 |
| DFW | $21,032,000 | 2 | $16,127,000 | $0 | $0 | $4,905,000 | $0 |
| DLH | $510,000 | 96 | $262,000 | $248,000 | $0 | $0 | $0 |
| DSM | $1,227,000 | 72 | $1,227,000 | $0 | $0 | $0 | $0 |
| DTW | $13,288,000 | 6 | $10,815,000 | $0 | $0 | $2,461,000 | $12,000 |
| DVT | $0 | 121 | $0 | $0 | $0 | $0 | $0 |
| ELP | $84,000 | 116 | $57,000 | $27,000 | $0 | $0 | $0 |
| EUG | $2,020,000 | 64 | $957,000 | $1,063,000 | $0 | $0 | $0 |
| EWR | $9,749,000 | 11 | $9,749,000 | $0 | $0 | $0 | $0 |
| EYW | $71,000 | 117 | $70,000 | $1,000 | $0 | $0 | $0 |
| FAI | $474,000 | 97 | $474,000 | $0 | $0 | $0 | $0 |
| FAT | $301,000 | 107 | $269,000 | $32,000 | $0 | $0 | $0 |
| FLL | $2,306,000 | 60 | $2,013,000 | $289,000 | $0 | $0 | $4,000 |
| FWA | $518,000 | 95 | $480,000 | $38,000 | $0 | $0 | $0 |
| FXE | $24,000 | 120 | $13,000 | $11,000 | $0 | $0 | $0 |
| GEG | $3,405,000 | 43 | $3,331,000 | $74,000 | $0 | $0 | $0 |
| GRR | $3,516,000 | 41 | $2,574,000 | $942,000 | $0 | $0 | $0 |
| GSO | $4,796,000 | 30 | $4,796,000 | $0 | $0 | $0 | $0 |
| GSP | $850,000 | 83 | $850,000 | $0 | $0 | $0 | $0 |
| HNL | $105,000 | 115 | $86,000 | $0 | $19,000 | $0 | $0 |
| HOU | $9,495,000 | 13 | $4,688,000 | $4,807,000 | $0 | $0 | $0 |
| HPN | $6,308,000 | 20 | $2,328,000 | $3,947,000 | $0 | $33,000 | $0 |
| HSV | $551,000 | 93 | $255,000 | $296,000 | $0 | $0 | $0 |
| IAD | $7,093,000 | 17 | $7,093,000 | $0 | $0 | $0 | $0 |
| IAH | $10,988,000 | 9 | $9,879,000 | $0 | $0 | $1,109,000 | $0 |
| ICT | $1,092,000 | 76 | $1,092,000 | $0 | $0 | $0 | $0 |
| ILN | $1,046,000 | 78 | $1,045,000 | $1,000 | $0 | $0 | $0 |
| IND | $2,834,000 | 55 | $2,834,000 | $0 | $0 | $0 | $0 |
| ISP | $3,726,000 | 40 | $2,855,000 | $871,000 | $0 | $0 | $0 |
| JAN | $336,000 | 105 | $333,000 | $3,000 | $0 | $0 | $0 |
| JAX | $1,778,000 | 66 | $1,773,000 | $5,000 | $0 | $0 | $0 |
| JFK | $4,270,000 | 36 | $4,268,000 | $0 | $0 | $0 | $2,000 |
| JNU | $411,000 | 99 | $0 | $103,000 | $308,000 | $0 | $0 |
| LAS | $31,000 | 118 | $27,000 | $4,000 | $0 | $0 | $0 |
| LAX | $6,752,000 | 18 | $6,752,000 | $0 | $0 | $0 | $0 |
| LCK | $137,000 | 113 | $79,000 | $58,000 | $0 | $0 | $0 |
| LGA | $13,568,000 | 5 | $12,296,000 | $0 | $1,272,000 | $0 | $0 |
| LGB | $2,647,000 | 57 | $926,000 | $1,589,000 | $0 | $0 | $132,000 |
| LIT | $554,000 | 92 | $457,000 | $97,000 | $0 | $0 | $0 |
| MCI | $4,000,000 | 37 | $4,000,000 | $0 | $0 | $0 | $0 |
| MCO | $3,066,000 | 50 | $2,318,000 | $0 | $0 | $748,000 | $0 |
| MDT | $1,464,000 | 68 | $1,063,000 | $401,000 | $0 | $0 | $0 |
| MDW | $16,033,000 | 3 | $13,714,000 | $2,319,000 | $0 | $0 | $0 |
| MEM | $6,431,000 | 19 | $6,331,000 | $0 | $0 | $49,000 | $51,000 |
| MHT | $6,212,000 | 21 | $5,485,000 | $727,000 | $0 | $0 | $0 |
| MIA | $3,082,000 | 48 | $3,082,000 | $0 | $0 | $0 | $0 |
| MKE | $5,061,000 | 27 | $4,843,000 | $6,000 | $0 | $204,000 | $8,000 |
| MMU | $264,000 | 109 | $95,000 | $169,000 | $0 | $0 | $0 |
| MSP | $6,041,000 | 22 | $6,041,000 | $0 | $0 | $0 | $0 |
| MSY | $2,895,000 | 54 | $2,725,000 | $170,000 | $0 | $0 | $0 |
| OAK | $1,080,000 | 77 | $791,000 | $289,000 | $0 | $0 | $0 |
| OKC | $2,222,000 | 62 | $2,114,000 | $108,000 | $0 | $0 | $0 |
| OMA | $1,115,000 | 75 | $1,115,000 | $0 | $0 | $0 | $0 |
| ONT | $364,000 | 101 | $364,000 | $0 | $0 | $0 | $0 |
| ORD | $23,601,000 | 1 | $23,039,000 | $0 | $0 | $562,000 | $0 |
| ORF | $4,702,000 | 32 | $3,614,000 | $1,064,000 | $0 | $24,000 | $0 |
| PBI | $780,000 | 85 | $635,000 | $145,000 | $0 | $0 | $0 |
| PDX | $3,030,000 | 51 | $2,735,000 | $294,000 | $0 | $0 | $1,000 |
| PHL | $5,772,000 | 23 | $5,145,000 | $0 | $0 | $627,000 | $0 |
| PHX | $3,082,000 | 49 | $1,375,000 | $1,707,000 | $0 | $0 | $0 |
| PIE | $352,000 | 102 | $165,000 | $187,000 | $0 | $0 | $0 |
| PIT | $8,132,000 | 15 | $8,132,000 | $0 | $0 | $0 | $0 |
| PVD | $4,348,000 | 35 | $2,413,000 | $1,935,000 | $0 | $0 | $0 |
| RDU | $3,873,000 | 38 | $3,868,000 | $2,000 | $0 | $0 | $3,000 |
| RFD | $851,000 | 82 | $257,000 | $594,000 | $0 | $0 | $0 |
| RIC | $3,133,000 | 47 | $3,022,000 | $91,000 | $0 | $20,000 | $0 |
| RNO | $597,000 | 89 | $523,000 | $74,000 | $0 | $0 | $0 |
| ROC | $993,000 | 80 | $687,000 | $9,000 | $0 | $297,000 | $0 |
| RSW | $5,610,000 | 24 | $2,915,000 | $2,695,000 | $0 | $0 | $0 |
| SAN | $671,000 | 88 | $0 | $0 | $671,000 | $0 | $0 |
| SAT | $2,074,000 | 63 | $1,895,000 | $179,000 | $0 | $0 | $0 |
| SDF | $560,000 | 91 | $560,000 | $0 | $0 | $0 | $0 |
| SEA | $8,761,000 | 14 | $7,304,000 | $0 | $0 | $1,457,000 | $0 |
| SFB | $171,000 | 111 | $98,000 | $73,000 | $0 | $0 | $0 |
| SFO | $2,253,000 | 61 | $2,225,000 | $28,000 | $0 | $0 | $0 |
| SHV | $342,000 | 104 | $342,000 | $0 | $0 | $0 | $0 |
| SJC | $4,718,000 | 31 | $2,559,000 | $2,159,000 | $0 | $0 | $0 |
| SLC | $3,812,000 | 39 | $3,783,000 | $0 | $0 | $0 | $29,000 |
| SMF | $2,974,000 | 52 | $2,674,000 | $300,000 | $0 | $0 | $0 |
| SNA | $3,353,000 | 44 | $103,000 | $3,250,000 | $0 | $0 | $0 |
| STL | $2,580,000 | 58 | $2,576,000 | $4,000 | $0 | $0 | $0 |
| SWF | $129,000 | 114 | $112,000 | $17,000 | $0 | $0 | $0 |
| SYR | $784,000 | 84 | $782,000 | $2,000 | $0 | $0 | $0 |
| TEB | $1,264,000 | 71 | $376,000 | $803,000 | $85,000 | $0 | $0 |
| TLH | $1,622,000 | 67 | $902,000 | $720,000 | $0 | $0 | $0 |
| TPA | $2,002,000 | 65 | $636,000 | $1,366,000 | $0 | $0 | $0 |
| TRI | $220,000 | 110 | $220,000 | $0 | $0 | $0 | $0 |
| TUL | $711,000 | 87 | $711,000 | $0 | $0 | $0 | $0 |
| TUS | $29,000 | 119 | $21,000 | $8,000 | $0 | $0 | $0 |
| TYS | $902,000 | 81 | $901,000 | $1,000 | $0 | $0 | $0 |
| VNY | $334,000 | 106 | $156,000 | $178,000 | $0 | $0 | $0 |
| Total | $429,302,000 |  | $363,058,000 | $43,163,000 | $5,960,000 | $16,879,000 | $242,000 |

Table 5b: Discounted 20 Year LAAS Passenger Time Savings – 100% WAAS Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Straight-In Approach | Takeoff Guidance | Complex Approach | ILS Critical Area | Parallel Approach |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $1,417,000 | 71 | $1,096,000 | $321,000 | $0 | $0 | $0 |
| ACK | $11,478,000 | 15 | $11,478,000 | $0 | $0 | $0 | $0 |
| AFW | $2,000 | 118 | $2,000 | $0 | $0 | $0 | $0 |
| ALB | $7,147,000 | 23 | $4,407,000 | $1,418,000 | $1,322,000 | $0 | $0 |
| ANC | $3,061,000 | 57 | $3,049,000 | $12,000 | $0 | $0 | $0 |
| ATL | $16,288,000 | 7 | $12,793,000 | $0 | $0 | $3,495,000 | $0 |
| AUS | $3,959,000 | 45 | $3,682,000 | $277,000 | $0 | $0 | $0 |
| AVL | $886,000 | 83 | $510,000 | $376,000 | $0 | $0 | $0 |
| BDL | $4,201,000 | 43 | $2,716,000 | $106,000 | $1,379,000 | $0 | $0 |
| BFI | $107,000 | 109 | $49,000 | $58,000 | $0 | $0 | $0 |
| BGR | $445,000 | 95 | $436,000 | $9,000 | $0 | $0 | $0 |
| BHM | $481,000 | 91 | $243,000 | $0 | $238,000 | $0 | $0 |
| BNA | $1,442,000 | 70 | $1,442,000 | $0 | $0 | $0 | $0 |
| BOI | $3,194,000 | 55 | $3,194,000 | $0 | $0 | $0 | $0 |
| BOS | $14,053,000 | 10 | $14,053,000 | $0 | $0 | $0 | $0 |
| BUF | $5,878,000 | 31 | $5,846,000 | $32,000 | $0 | $0 | $0 |
| BUR | $731,000 | 87 | $21,000 | $392,000 | $318,000 | $0 | $0 |
| BWI | $6,470,000 | 26 | $6,470,000 | $0 | $0 | $0 | $0 |
| CAE | $1,121,000 | 78 | $1,120,000 | $1,000 | $0 | $0 | $0 |
| CHA | $344,000 | 102 | $344,000 | $0 | $0 | $0 | $0 |
| CHS | $1,721,000 | 68 | $1,721,000 | $0 | $0 | $0 | $0 |
| CLE | $6,731,000 | 25 | $6,731,000 | $0 | $0 | $0 | $0 |
| CLT | $14,739,000 | 8 | $14,739,000 | $0 | $0 | $0 | $0 |
| CMH | $4,309,000 | 42 | $3,564,000 | $745,000 | $0 | $0 | $0 |
| COS | $6,456,000 | 27 | $4,229,000 | $2,227,000 | $0 | $0 | $0 |
| CVG | $12,295,000 | 11 | $9,997,000 | $0 | $0 | $2,298,000 | $0 |
| DAB | $450,000 | 94 | $254,000 | $196,000 | $0 | $0 | $0 |
| DAL | $3,124,000 | 56 | $1,697,000 | $1,427,000 | $0 | $0 | $0 |
| DAY | $1,397,000 | 72 | $1,317,000 | $1,000 | $0 | $79,000 | $0 |
| DCA | $3,691,000 | 50 | $2,340,000 | $0 | $1,351,000 | $0 | $0 |
| DEN | $19,332,000 | 4 | $19,332,000 | $0 | $0 | $0 | $0 |
| DFW | $28,953,000 | 2 | $21,097,000 | $0 | $0 | $7,856,000 | $0 |
| DLH | $509,000 | 90 | $319,000 | $190,000 | $0 | $0 | $0 |
| DSM | $1,392,000 | 73 | $1,392,000 | $0 | $0 | $0 | $0 |
| DTW | $18,350,000 | 5 | $14,258,000 | $0 | $0 | $4,091,000 | $1,000 |
| DVT | $0 | 119 | $0 | $0 | $0 | $0 | $0 |
| ELP | $101,000 | 111 | $71,000 | $30,000 | $0 | $0 | $0 |
| EUG | $2,146,000 | 66 | $1,222,000 | $924,000 | $0 | $0 | $0 |
| EWR | $12,052,000 | 13 | $12,052,000 | $0 | $0 | $0 | $0 |
| EYW | $104,000 | 110 | $103,000 | $1,000 | $0 | $0 | $0 |
| FAI | $465,000 | 93 | $465,000 | $0 | $0 | $0 | $0 |
| FAT | $429,000 | 97 | $399,000 | $30,000 | $0 | $0 | $0 |
| FLL | $3,019,000 | 58 | $2,610,000 | $408,000 | $0 | $0 | $1,000 |
| FWA | $471,000 | 92 | $458,000 | $13,000 | $0 | $0 | $0 |
| FXE | $5,000 | 117 | $2,000 | $3,000 | $0 | $0 | $0 |
| GEG | $3,814,000 | 49 | $3,742,000 | $72,000 | $0 | $0 | $0 |
| GRR | $3,833,000 | 48 | $3,057,000 | $776,000 | $0 | $0 | $0 |
| GSO | $5,751,000 | 32 | $5,751,000 | $0 | $0 | $0 | $0 |
| GSP | $1,162,000 | 77 | $1,162,000 | $0 | $0 | $0 | $0 |
| HNL | $167,000 | 106 | $135,000 | $0 | $32,000 | $0 | $0 |
| HOU | $12,178,000 | 12 | $5,769,000 | $6,409,000 | $0 | $0 | $0 |
| HPN | $5,283,000 | 35 | $2,734,000 | $2,511,000 | $0 | $38,000 | $0 |
| HSV | $563,000 | 89 | $306,000 | $257,000 | $0 | $0 | $0 |
| IAD | $9,718,000 | 17 | $9,718,000 | $0 | $0 | $0 | $0 |
| IAH | $14,353,000 | 9 | $13,006,000 | $0 | $0 | $1,347,000 | $0 |
| ICT | $1,102,000 | 79 | $1,102,000 | $0 | $0 | $0 | $0 |
| ILN | $0 | 120 | $0 | $0 | $0 | $0 | $0 |
| IND | $2,393,000 | 62 | $2,393,000 | $0 | $0 | $0 | $0 |
| ISP | $5,416,000 | 34 | $4,046,000 | $1,370,000 | $0 | $0 | $0 |
| JAN | $395,000 | 99 | $392,000 | $3,000 | $0 | $0 | $0 |
| JAX | $2,160,000 | 65 | $2,154,000 | $6,000 | $0 | $0 | $0 |
| JFK | $5,250,000 | 36 | $5,250,000 | $0 | $0 | $0 | $0 |
| JNU | $357,000 | 101 | $0 | $101,000 | $256,000 | $0 | $0 |
| LAS | $42,000 | 115 | $36,000 | $6,000 | $0 | $0 | $0 |
| LAX | $8,693,000 | 18 | $8,693,000 | $0 | $0 | $0 | $0 |
| LCK | $0 | 121 | $0 | $0 | $0 | $0 | $0 |
| LGA | $18,318,000 | 6 | $16,601,000 | $0 | $1,717,000 | $0 | $0 |
| LGB | $2,230,000 | 64 | $894,000 | $1,320,000 | $0 | $0 | $16,000 |
| LIT | $643,000 | 88 | $551,000 | $92,000 | $0 | $0 | $0 |
| MCI | $5,096,000 | 38 | $5,096,000 | $0 | $0 | $0 | $0 |
| MCO | $4,147,000 | 44 | $2,997,000 | $0 | $0 | $1,150,000 | $0 |
| MDT | $1,665,000 | 69 | $1,284,000 | $381,000 | $0 | $0 | $0 |
| MDW | $22,039,000 | 3 | $18,084,000 | $3,955,000 | $0 | $0 | $0 |
| MEM | $5,490,000 | 33 | $5,445,000 | $0 | $0 | $39,000 | $6,000 |
| MHT | $7,506,000 | 21 | $6,598,000 | $908,000 | $0 | $0 | $0 |
| MIA | $3,678,000 | 51 | $3,678,000 | $0 | $0 | $0 | $0 |
| MKE | $6,732,000 | 24 | $6,451,000 | $6,000 | $0 | $274,000 | $1,000 |
| MMU | $57,000 | 114 | $16,000 | $41,000 | $0 | $0 | $0 |
| MSP | $7,927,000 | 19 | $7,927,000 | $0 | $0 | $0 | $0 |
| MSY | $3,652,000 | 52 | $3,401,000 | $251,000 | $0 | $0 | $0 |
| OAK | $1,165,000 | 76 | $830,000 | $335,000 | $0 | $0 | $0 |
| OKC | $2,662,000 | 61 | $2,539,000 | $123,000 | $0 | $0 | $0 |
| OMA | $1,222,000 | 75 | $1,222,000 | $0 | $0 | $0 | $0 |
| ONT | $399,000 | 98 | $399,000 | $0 | $0 | $0 | $0 |
| ORD | $30,997,000 | 1 | $30,070,000 | $0 | $0 | $927,000 | $0 |
| ORF | $6,120,000 | 29 | $4,708,000 | $1,388,000 | $0 | $24,000 | $0 |
| PBI | $899,000 | 82 | $762,000 | $137,000 | $0 | $0 | $0 |
| PDX | $3,855,000 | 46 | $3,469,000 | $386,000 | $0 | $0 | $0 |
| PHL | $7,398,000 | 22 | $6,452,000 | $0 | $0 | $946,000 | $0 |
| PHX | $4,441,000 | 41 | $1,787,000 | $2,654,000 | $0 | $0 | $0 |
| PIE | $182,000 | 105 | $107,000 | $75,000 | $0 | $0 | $0 |
| PIT | $10,901,000 | 16 | $10,901,000 | $0 | $0 | $0 | $0 |
| PVD | $6,083,000 | 30 | $3,246,000 | $2,837,000 | $0 | $0 | $0 |
| RDU | $5,246,000 | 37 | $5,243,000 | $3,000 | $0 | $0 | $0 |
| RFD | $70,000 | 113 | $29,000 | $41,000 | $0 | $0 | $0 |
| RIC | $3,840,000 | 47 | $3,719,000 | $102,000 | $0 | $19,000 | $0 |
| RNO | $734,000 | 86 | $639,000 | $95,000 | $0 | $0 | $0 |
| ROC | $1,235,000 | 74 | $837,000 | $10,000 | $0 | $388,000 | $0 |
| RSW | $7,757,000 | 20 | $3,781,000 | $3,976,000 | $0 | $0 | $0 |
| SAN | $851,000 | 85 | $0 | $0 | $851,000 | $0 | $0 |
| SAT | $2,331,000 | 63 | $2,133,000 | $198,000 | $0 | $0 | $0 |
| SDF | $387,000 | 100 | $387,000 | $0 | $0 | $0 | $0 |
| SEA | $11,704,000 | 14 | $9,536,000 | $0 | $0 | $2,168,000 | $0 |
| SFB | $152,000 | 108 | $119,000 | $33,000 | $0 | $0 | $0 |
| SFO | $2,908,000 | 60 | $2,863,000 | $45,000 | $0 | $0 | $0 |
| SHV | $437,000 | 96 | $437,000 | $0 | $0 | $0 | $0 |
| SJC | $6,390,000 | 28 | $3,163,000 | $3,227,000 | $0 | $0 | $0 |
| SLC | $4,696,000 | 40 | $4,693,000 | $0 | $0 | $0 | $3,000 |
| SMF | $3,651,000 | 53 | $3,238,000 | $413,000 | $0 | $0 | $0 |
| SNA | $4,700,000 | 39 | $56,000 | $4,644,000 | $0 | $0 | $0 |
| STL | $3,407,000 | 54 | $3,400,000 | $7,000 | $0 | $0 | $0 |
| SWF | $163,000 | 107 | $152,000 | $11,000 | $0 | $0 | $0 |
| SYR | $1,030,000 | 81 | $1,028,000 | $2,000 | $0 | $0 | $0 |
| TEB | $272,000 | 104 | $65,000 | $192,000 | $15,000 | $0 | $0 |
| TLH | $1,799,000 | 67 | $1,225,000 | $574,000 | $0 | $0 | $0 |
| TPA | $2,934,000 | 59 | $838,000 | $2,096,000 | $0 | $0 | $0 |
| TRI | $296,000 | 103 | $296,000 | $0 | $0 | $0 | $0 |
| TUL | $874,000 | 84 | $874,000 | $0 | $0 | $0 | $0 |
| TUS | $34,000 | 116 | $25,000 | $9,000 | $0 | $0 | $0 |
| TYS | $1,097,000 | 80 | $1,096,000 | $1,000 | $0 | $0 | $0 |
| VNY | $71,000 | 112 | $28,000 | $43,000 | $0 | $0 | $0 |
| Total | $542,146,000 |  | $458,181,000 | $51,319,000 | $7,479,000 | $25,139,000 | $28,000 |

## Reduced Disruptions for Straight-in Precision Approaches

In the LAAS Navigation Capabilities Baseline, IBM identified a set of operational capabilities for which LAAS is expected to provide a benefit.  Two of these operational capabilities are precision approaches down to Cat I minima and Cat II/III minima, respectively.  The operational justification for the benefits arises from the expectation that 1) LAAS Cat I will reduce the landing minima at runways without Cat I service and 2) LAAS Cat II/III will reduce minima at runways without a corresponding ILS Cat II or III capability.

In instrument meteorological conditions (IMC), if a runway has no precision approach, instrument approaches must be conducted using non-precision approach (NPA) procedures. The minima for such procedures are typically a ceiling of 400 to 500 feet and 1 mile visibility (without approach lights).  LAAS Cat I is expected to be able to support precision approaches down to a 200 foot Decision Height (DH) and 1/2 mile visibility (with approach lights). This lowering of minima can result in fewer 1) flight cancellations, 2) diversions to alternate airports, and 3) delays, all of which can occur when a pilot cannot see the runway at the decision height or the airport shuts down the runway due to visibility below minima for the available approaches.  These types of disruptions can be very costly to the users, particularly the scheduled airlines, and can lead to major problems at the local airport as well as regionally or even nationally.  Further, assuming that a LAAS Cat II capability is developed that meets the more stringent performance requirements for Cat II operations, it will be possible to achieve a ceiling/visibility reduction down to a 100 foot DH and 1200 foot runway visual range (RVR) (with lights and other supporting infrastructure).  Similarly, further development is expected to result in LAAS achieving Cat III minima.

In this section, the methodology that IBM used to calculate the monetary value of the benefit achieved for straight-in approaches from a reduction in disrupted flights is described.  The methodology is based on analytical approaches used to derive similar benefits for the Microwave Landing System and for the European Geostationary Navigation Overlay Service (EGNOS).  Note that although the methodology is being described for straight-in approaches, it was also used to calculate the benefits from complex approaches, assuming that these approaches result in further reductions in approach minima (e.g., by achieving separation from obstacles which currently limit straight-in approach minima) and they are approved for LAAS by the FAA.

Although the horizontal and vertical navigational accuracy achieved with LAAS is expected to be greater than that obtained with ILS, the FAA has decided to use the ILS TERPS criteria for initial LAAS approach implementations.  This will result in the approach minima being the same for both ILS and LAAS.  If the TERPS surfaces are later adjusted to take advantage of the improved accuracy of LAAS, either for the approach or the missed approach segments, the associated minima may be reduced below the minima for ILS.  Consequently, for this analysis of straight-in approach benefits, LAAS was assumed to offer no improvement over existing ILS minima.

### Derivation of the Mathematical Formula for Calculating Straight-in Approach Benefits

### Preprocessing Step

The derivation of the mathematical formula begins with a preprocessing step to tailor the list of runways considered in the analysis to include only those that are appropriate candidates for LAAS benefits.  There are a total of 716 runways at the 121 airports selected for this study.  Runways that are not eligible candidates for possible improvement from LAAS Cat I or Cat II/III are discarded from consideration.  These eliminated runways include the following:

- Runways not currently used or planned to be used for arrivals

- Runways that are less than 4200 feet in length, the shortest acceptable runway length for a precision approach

- For LAAS Cat I, all runways equipped, or planned to be equipped prior to 2009, with an ILS, since LAAS is not expected to offer any improvement in these circumstances

- For LAAS Cat II/III, all runways equipped with a Cat II or Cat III ILS

- One runway from set of parallel runways if the centerline spacing is less than 4300 feet

### In addition to the elimination of these runways, an airport (along with its associated runways) was removed if the projected demand for airport resources is sufficiently less than the IMC capacity of the airport.

There are several possible methods for calculating the demand/capacity ratio of any airport.  IBM has selected the following approach for its simplicity and availability of relevant data:

- For each airport, determine the maximum sustainable arrival throughput during different weather conditions using Enhanced Traffic Management System (ETMS) traffic data and National Climatic Data Center (NCDC) weather data for CY2000. Since VFR flights are not captured in ETMS data, this method is not applicable to a few airports that have significant VFR traffic (e.g., ACK).

- Calculate the percent drop in observed throughput from VMC to IMC for each airport.  A previous IBM analysis that calculated theoretical throughput change from VMC to IMC found that up to a 9% drop is expected based solely on required changes in longitudinal separations between arrivals.  Thus, an observed drop of 10% or greater is likely to be associated with operational issues that LAAS may be able to address.

- If the airport’s throughput drops by less than 10% from VMC to IMC, then there is considered to be little that LAAS can provide as an incremental benefit from reduced straight-in disruptions. This airport and its associated runways are removed from consideration.

### Mathematical Formulation of the Straight-in Approach Benefits

To quantify the benefits that may be achieved by LAAS from the reduction in arrival disruptions due to lower approach minima, two values must be derived:

- the number of disruptions avoidable with LAAS

- the monetary savings obtained from each avoided disruption

The product of these two values yields the benefit that can be expected from the lower minima achievable with LAAS over what is possible with the baseline systems (see Appendix F for a listing of baseline systems).  In this report, it is assumed that the baseline consists of existing and planned technologies, and does not include those that might be justified, but are not currently included in the FAA’s plans.  The total benefit is obtained by summing this product over three dimensions:

- each year in the 20-year time horizon of this study

- each runway that passed successfully through the preprocessing filter described above

- all user groups (i.e., major passenger airlines, major cargo airlines, regional airlines, corporate jet aircraft, and small GA aircraft in Alaska)

Expressed mathematically, this product and sum appear as follows:

where B is the LAAS benefit for straight-in approaches, i is the year, j is the runway, k is the user group, is the total number of avoidable disruptions in year i at runway j by user group k, and is the monetary operational savings obtained from each avoided disruption in year i by user group k.

It should be noted that this formula gives the total operational benefit for the various user groups, but does not include the benefit to the passengers.  That benefit, based on the PTS is calculated similarly except that is replaced with, the PTS from each avoided disruption in year i by user group k.  PTS benefits are calculated for all user groups except cargo airlines.

### Derivation of the Number of Disruptions Avoidable with LAAS

To derive the number of disruptions that can be avoided with LAAS, the number can be broken down into its various components.  This number can be expressed as follows:

where;

is the total number of avoidable disruptions in year i, on runway j, by user group k,

is the number of arrivals at this airport in year i by user group k,

is the probability that runway j will be used for arrivals of user group k,

is the probability that the weather at this airport is between the minima in ceiling and visibility for LAAS Cat X (where X is either I, II/III) and the Baseline navigation system on runway j,

is the probability that the weather at this airport is between the minima in ceiling and visibility for LAAS Cat X and the Next Best baseline navigation system on runway j,

is the probability that LAAS Cat X is available,

is the probability that the Baseline system is available (Next Best baseline system is assumed to be 100% available),

is the probability that an aircraft in group k will be equipped and its pilots trained and certified on LAAS Cat X in year i,

is the probability that an aircraft in group k will be equipped and its pilots trained and certified on the Baseline system in year i (Next Best baseline system is assumed to be 100% equipped), and

is a factor to account for the ripple, or downstream effects of each disruption.

As can be seen from this equation, the focus of the calculation is on individual runways rather than the entire airport.  This is due to the runway-specific nature of some of the baseline technologies, and the fact that approach minima are runway-specific.  Therefore, the benefits must be calculated at this level of detail and then aggregated to the airport level.

The annual number of arrivals () can be obtained in various ways.  In this study the Official Airline Guide (OAG) was used to obtain the current demand for major passenger airlines and regional airlines and growth factors from the FAA’s Terminal Area Forecasts (TAF) were applied to derive the demand in future years.  A similar method can be used to extrapolate from current to future years for major cargo airlines, corporate aircraft, and low-end general aviation aircraft in Alaska.  Since cargo carriers, air taxi operators, and GA operators do not publish schedules in the OAG, the baseline year was obtained from other sources (e.g., from cargo airlines themselves, ETMS data, DOT Transtat website).

Since the approach and landing capabilities are focused on individual runways, it is necessary to determine the number of these avoided disruptions that should be allocated to runway j.  A logical way to approach this problem is to determine the probability that each runway is or will be used in IMC conditions () and to multiply this factor by the number of avoided disruptions for the entire airport.  Although the Aviation System Performance Metrics (ASPM) database contains information on runway configuration use under various weather conditions, it is available for only 46 airports and, moreover, the frequency of use of the individual runways within each configuration is unknown.  Therefore, runway usage for all 121 airports must be derived based on available data, including wind direction, runway length, and ILS placement.  When possible, these derived runway usage estimates were validated against runway usage observations, (e.g., some individual Airport Capacity Enhancement Plans) and with airport operations representatives.  Full details of the method used to derive runway utilization estimates are reported in Appendix M.

Recognizing that in most situations, airports favor one or two runways in IMC and therefore these runways account for a disproportional number of approaches,  also takes into account the likelihood that an approaching aircraft will be routed to runway j as opposed to another alternative.   When the wind is less than 10 knots making it possible for multiple runways to be used for approaches despite the wind direction, the principal runway(s) are assigned 70% of the traffic and the secondary runway(s) get 30%.  These percentages are based on actual observations of runway use and were documented in previous FAA benefits studies  and FAA guidance.   is modified to take account of the fact that not all aircraft for user group k may be capable of landing on runway j since the runway may not be long enough to accommodate a certain aircraft type.

To obtain the value for the probability of the weather being between two minima ( or ), IBM accessed the observed ceiling and visibility information for the 121 airports from the NCDC database for the years 1998 to 2001.  Instead of including weather for a 24-hour time period, only weather during the typical traffic day, 7AM to 10 PM, was used.  Since the ceiling data was only available in 100 foot increments, it was necessary to use an interpolation to derive the probability of weather for finer levels of gradation (e.g., 50 foot increments).  The ceiling and visibility minima associated with the baseline systems and LAAS were obtained from two sources: published instrument approaches whenever available and alternatively, the output from model runs conducted by the MITRE/CAASD with its GAME model.  It should be mentioned here that the possibility exists that users may not be 100% equipped with the best baseline alternative system at each airport, and so the derivation of  must take this possibility into account by also considering the next best alternative.

Since the benefit of avoided disruptions from lower minima can be achieved only when LAAS is available and aircraft are equipped, it is necessary to include factors for the availability () and probability of being equipped () in the equation. The availability and equipage of the best baseline system are also taken into consideration.  The pace of expected avionics equipage was estimated through surveys and interviews conducted with representatives from the user communities, and resulted in a range of values used in the sensitivity analysis (see Appendix D for details on how the pace of equipage was incorporated into the sensitivity analysis, see Appendix F for the expected avionics equipage values used).

Finally, a factor to account for the downstream effects of disruptions is applied to obtain the total number of avoided disruptions. See Appendix D for a description of how the downstream effect of delays factor was incorporated into the sensitivity analysis.

### Derivation of Savings Obtained from Avoided Disruptions

To derive the savings that can be obtained from avoided disruptions in year i by user group k, the number can be broken down into its components.  This number can be expressed as follows:

where;

is the average cost of a disruption in the year 2004 to user group k and

is the discount factor in year i relative to the year 2004,

and r is the appropriate discount rate.

The average cost of a disruption to user group k () is calculated by taking the sum of the costs of a delay, cancellation, and diversion weighed by the frequency of their occurrence over a specified past period.  The derivation of these disruption costs is detailed in Appendix C.  For major and regional passenger airlines, disruption information was obtained from the Airline Service Quality Program (ASQP) database for the years 1998 through 2003.  For cargo carriers, cancellations were set to zero based on airline representative input and the ASQP disruption rates for major passenger airlines were applied for diversions and delays.  For GA operators, cancellations were set to zero, and ASQP disruption rates for regional passenger airlines were applied for diversions and delays.  An inflation factor, based on OMB guidance, was applied to derive the costs for 2004, the baseline year for this analysis.

The factoris multiplied by to ensure that the future saved cost of an avoided disruption is appropriately discounted, reflecting the reduction in present value the longer the benefit is deferred.  A real discount rate of 7% was used, based on guidance from the OMB.

### Example

Washington’s Reagan National airport (DCA) is used to illustrate how the mathematical formula is applied to obtain the LAAS benefit.  DCA has 6 runways (01/19, 15/33, 04/22).  All 6 runways are used for approaches and only 01 is equipped with an ILS (Cat II).  DCA runways 19, 04, 22, 15, and 33 have a variety of non-precision (e.g., VOR/DME and GPS) approaches with minimum decision heights ranging from 587 to 904 feet. An opportunity exists to reduce the ceiling and visibility minima on these runways with LAAS Cat I, if the users do not equip with WAAS.

To simplify this example, it will focus on a single year (i = 2020), single runway (j = DCA 15), and single user group (k = corporate jet operators).  Although GA volume has been restricted at DCA since 9/11/01, the FAA’s 2004 TAF shows a small amount of future GA volume at DCA which was considered in this example.  Note that since DCA 15 is only 5204 feet long, it is not appropriate for all users, such as major passenger airlines and others who operate aircraft too large to land on this runway. Based on the methodology described above, the parameters in Table 6 were obtained.  Note that the benefit for this year, runway, and user group is obtained by simply multiplying the first 8 parameters.  To obtain the Cat I benefit for the entire airport, the discounted benefits for the 20 year period is summed over all runways and all user groups.

Table 6:  key parameter values for DCA 15 example

| # of DCA arrivals (Corporate jet Operators) | % of time between LAAS and Baseline minima | Utilization of DCA runway 15 (Corporate jet Operators) | Availability of LAAS | LAAS equipage | Cost of disruption (Corporate jet Operators) | Discount factor for 2020 | Ripple Effect Factor | Direct Operating Cost Benefit (Corporate jet Operators) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 710 | .05 | .07 | .999 | 1.0 | $502 | .34 | 1.8 | $760 |

### Results

Tables 7A and 7B show the total straight-in LAAS approach benefit estimated for the 121 airports studied.  Table 7A shows these benefits for Cat I LAAS implementation, in terms of both reduced direct operating costs and passenger time savings, as well as for the two scenarios of user WAAS equipage.  Table 7B shows these benefits for Cat II/III LAAS implementation, above and beyond those for Cat I.  Total straight-in benefits are obtained by adding corresponding cells from Tables 7A and 7B (e.g., total DOC benefit for 0% WAAS is $ 448.2M = $87.7M + $360.5M)

Table 7a: Discounted 20 year LAAS Straight-in Benefits for Cat I

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $87,700,000 | $107,700,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $2,500,000 | $2,900,000 |

Table 7b: Discounted 20 year LAAS Straight-in Benefits for Cat II/III

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $360,500,000 | $455,200,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $360,500,000 | $455,200,000 |

## Reduced Disruptions with LAAS Takeoff Guidance

A restricted ability to perform departure operations during low visibility conditions, although rare, can be highly disruptive to airport and airline operations. When low visibility conditions coincide with an airport’s departure bank, particularly early in the day, the impact can be significant.  In some cases it can take more than a full day for an airline’s operations to recover from the disruption to their system resulting from such an event.

Current rules governing takeoff under low visibility conditions permit operations in various Runway Visual Range (RVR) conditions depending on several factors, including runway markings, lighting, RVR measurement equipment, surface movement guidance and control plans, and aircrew training.  Takeoff operations in very low visibility conditions may be conducted with the use of a takeoff guidance system, (e.g., Cat III ILS localizer for front-course guidance and a head up display (HUD)).  It is expected that LAAS Cat II/III, as part of a takeoff guidance system, will also provide this level of guidance, potentially at far more runways than are currently served by Cat III localizers.  LAAS and HUD equipped users benefit directly by continuing takeoff operations during these conditions, and all airport users benefit indirectly from the reduced time required for the airport to restore normal operations once low visibility conditions end (due to a smaller backlog of aircraft waiting to depart).

Airports with multiple Cat III localizers will accrue benefit from this LAAS capability only if demand is sufficiently high to warrant the use of multiple departure runways under these conditions and if operational and safety considerations permit departures from multiple runways under these conditions.  Airports with only a single Cat III localizer will benefit from this capability by continuing to perform simultaneous arrivals and departures by using the Cat III ILS runway for arrivals and using LAAS on one of the other runways for departures.  Airports currently lacking Cat III localizers and airports with a single Cat III localizer may benefit significantly from this LAAS capability, and this analysis is limited to such airports.

Within the 121 airports studied, 22 airports have more than one Cat III localizer.  Of the remaining 99 airports, existing infrastructure supports takeoff operations at 300, 500, 1000, and 1600 RVR at 1, 49, 3, and 46 airports respectively.  Users equipped with a LAAS-based takeoff guidance system may be able to benefit at these 99 airports.

Figure 2 shows the distribution of low visibility conditions during the day for the airports with no Cat III ILSs.  Although these conditions are observed at all times of day, the majority occur during the early morning, when the impact on an airline’s operation is greatest.

Figure 2. Time Distribution of Low Visibility Conditions among Airports with no Cat III ILS.

### Methodology

In order to investigate the delay savings that may be achieved by using LAAS for takeoff guidance, the lowest takeoff minima supported by each airport had to be determined, including the timing and duration of low visibility conditions.  That information was then combined with departure demand.  Following that, an airport delay model was employed to estimate the expected delays both with and without LAAS-guided takeoffs.  In this analysis, the impact of LAAS was modeled as the ability of the airport to maintain IMC departure rates, for aircraft equipped with both Cat III LAAS and HUD, in the presence of very low visibility conditions.  The methodology consisted of the following steps:

- Obtain the required data:

  - Airports with one or no Cat III localizer

  - The lowest takeoff minima supported by each non-Cat III localizer runway at an airport

  - The number of hours per year that each airport experiences visibility conditions below these minima

  - The IMC and VMC departure capacity of each airport

  - The total departure traffic at each airport for a typical day

- Run IBM’s Single Airport Delay Model to calculate departure delay for two scenarios, with and without LAAS, accounting for the timing and duration of low visibility conditions:

- Calculate the average annual change in delay:

  - Take the difference between delays per flight in the two scenarios

  - Multiply this difference in delay per flight by the average daily traffic volume

  - Multiply this daily change in delay by the number of days with low visibility conditions

- Multiply by the percentages of LAAS and HUD avionics equipage levels and divide by 2 to get the portion attributable to LAAS

- Multiply by the downstream effect factor for takeoff delays (see Appendix N)

- Multiply by .999, the assumed availability of LAAS

- Multiply the minutes of delay by the cost of ground delay per minute for each user type

### Limitations

Following takeoff, LAAS may be able to provide precision departure guidance, including procedural separation, on straight or curved departure paths, potentially allowing for a higher rate of departure operations under low visibility conditions than is possible with localizer guidance and radar vectoring   area navigation (RNAV) departure procedures, using existing avionics and ground systems, may also provide much of this benefit.  Thus, the impact of this LAAS capability is difficult to evaluate.

Installation of Cat III ILS at runways receiving this LAAS benefit would eliminate this benefit.

### Results

Table 8 shows the total LAAS takeoff guidance benefit estimated for the 121 airports studied.  The table shows these benefits for Cat II/III LAAS implementation, in terms of both reduced direct operating costs and passenger time savings, as well as for the two scenarios of user WAAS equipage.

Table 8: Discounted 20 year LAAS Takeoff Guidance Benefits for Cat II/III

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $43,200,000 | $51,300,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $43,200,000 | $51,300,000 |

## Benefits from LAAS-based Complex Procedures

In addition to providing final approach guidance for straight-in approaches, LAAS is also capable of supporting complex RNAV procedures.  However, a variety of other existing and planned avionics and ground systems may also support such procedures.  RNAV procedures conducted without LAAS are reportedly capable of supporting complex operations down to near-Cat I approach minima, and if linked to an ILS final approach, down to the minima supported by the ILS.  LAAS offers the possibility of conducting complex procedures down to Cat I or Cat II/III minima where no ILS is available, as well as the simplicity of using a single system for terminal area navigation through final approach and landing, potentially down to Cat III minima.  Discussions with major airline representatives have shown that simplification of terminal area and landing procedures is a primary goal.  Further, these airlines view GPS-based RNAV/RNP as the navigation solution down to near-Cat-I operations and LAAS-based RNAV/RNP as the desired transition from GPS to (Global Navigation Satellite System [GNSS] Landing System) GLS down to Cat-III operations.  Based on this input, LAAS-based complex approach benefits were evaluated only in those cases where no ILS is present and only for weather conditions worse than those supported by baseline system approach minima.

LAAS may support complex operations either through use of the LAAS position-velocity-time signal (PVT) as an input to an on-board navigator, or through the direct broadcast of waypoints from the LAAS Ground Facility (LGF).  In the former, LAAS may provide improved ANP in the terminal area, and thus may support more stringent required RNP procedures than other systems (e.g., un-augmented GPS).  This benefit may not be limited to improved approach procedures, but may apply more generally to airspace management, with very low RNP routes supported by LAAS, including highly precise vertical restrictions.  Such routes have the potential to resolve existing airspace conflicts, both within a single airports operations (e.g., more precise separation of arrival and departure streams at SEA), and among closely situated airports (e.g., runway use conflicts between ORD and MDW, SEA and BFI, or JFK, LGA, EWR, and TEB). However, at this time RNP levels have not been established for these procedures, and thus it is not possible to discern which requirements are beyond the capabilities of existing systems and which will require LAAS. Further, it is anticipated that the RNP will vary within the approach (and departure) environment, and thus the transition point in the procedures from a GPS-based RNAV/RNP to a LAAS-based RNAV/RNP is not clear.  Until these RNP levels are established, the extent of LAAS-enabled RNAV benefits will remain unclear.

Additionally, LAAS is expected to provide increased availability of small RNP values.  Low RNP values are currently limited by the flight technical error, rather than the navigation system, which makes it difficult to assign any benefit for reducing the RNP values to LAAS.  However, the limiting factor on the availability of low RNP values is the navigation system and the equivalent-Receiver Autonomous Integrity Monitoring (RAIM) performance, which LAAS is expected to improve.  The availability of RNP-0.15 ranges from 98% to 80% depending on the number of GPS satellites that are operational.  LAAS is expected to increase that availability to 99.9% or better, except in the 100% WAAS equipage scenario, in which case this benefit may be provided by WAAS.  This benefit is not quantified in this analysis.

The appeal of direct broadcast of waypoints, or data uplink, for complex procedures is twofold. First, since the source of the procedure is local to the airport, uplink eliminates concerns about version control of procedures among different aircraft (that is, with an onboard database of procedures, and each operator potentially updating procedures at a different pace, there is a concern that two or more versions of a single procedure can be in use simultaneously). Second, uplink of procedures may reduce the burden placed on the onboard database for some aircraft. The costs of adding and certifying increased storage capacity can be significant.  Further, as the number of procedures, including terminal area, en-route and high-altitude routes, continues to increase, operators may be forced to choose between the expense of database upgrades and the operational complexity of isolating certain aircraft to particular regions.  Since the specific storage requirements for onboard versus uplinked procedures are not yet defined (i.e., even with uplink available, procedures may need to be stored in an onboard database for other purposes), this benefit of uplink is not clear, and therefore is not quantified in this analysis.

In the absence of RNAV procedures, flight paths within the terminal area during IMC are controlled by vectoring, a process that involves a high level of air-to-ground communication and that can result in a broad range of paths flown by individual aircraft.  Reducing both the communications workload and the variability in the time and distance flown in the terminal area are of great interest to controllers, pilots and airlines.  RNAV/RNP procedures have the potential to significantly reduce the communications component of this overall workload. Since these procedures follow pre-set routes, the pilots can focus on flight operations to follow the routes and the controller can focus on surveillance. Further communications should only be necessary in the event that the aircraft diverges from the assigned route, or the controller determines that a deviation is necessary.  One study of RNAV terminal procedure development at Philadelphia found that pilot-controller communications fell by over 60%, from 16 separate communications required for vectoring to just 6 with RNAV routes. The time and attention saved by eliminating these 10 communications can now be focused on flying, and monitoring, the RNAV route.  While LAAS may contribute to the conduct of RNAV and RNP procedures, the ability of other systems in the baseline to provide similar services eliminates this as an incremental LAAS benefit.

Reductions in flight time variability could yield significant benefits in terms of direct operating cost saved, improved customer service and on-time performance, and improved predictability of arrival times for the airlines’ gate operations. The value of predictability was described well by David Knorr et al: “Predictability measures the variation in the [Air Traffic Management] ATM system as experienced by the user. Commercial airlines may benefit as much from a reduction in the variance (or an improvement in the consistency) of flight/taxi times as they would from a reduction in average flight times. System predictability allows for improved scheduling and more efficient bank operations.” Other aviation industry representatives and researchers have also pointed out the high value of predictability to commercial airlines.  Additionally, it is one of the goals in the FAA’s Flight Plan 2004-2008 to “achieve greater conformity between expected and actual flight times.”   Potential benefits from reduced flight time variability are of particular importance at the nation’s busiest airports, due to the high volume of traffic handled, and to the related importance for airlines to carefully time their operations.  Earlier work by IBM showed that flight time variability in the terminal area for arrivals to ORD 9L is as much as 13 minutes, depending on what vectoring path is assigned, and that a proposed RNP procedure for this runway could reduce this variability nearly to zero.  However, as was the case for the benefits associated with communication workload, while LAAS may contribute to the conduct of such RNP procedures, the ability of other systems in the baseline to provide similar service eliminates this as an incremental LAAS benefit.

### Estimated Complex Approach Benefit

As stated above, most terminal area complex operations can be accomplished with existing or planned avionics and ground systems, without the need for LAAS.  Even complex procedures ending with a precision approach may be performed by transitioning to an existing ILS for the final approach and landing.  This section explores the benefits available to LAAS at those runways that do not have an ILS and that did not receive any Cat II/III benefit in the Straight-In Approach section of this work, and had no, or limited, Cat I benefit due to relatively high estimated decision heights associated with LAAS.  These runways include candidates such as JNU 8 and 26, as well as DCA 19, which for reasons of terrain or airspace restrictions cannot have an ILS installation.  The following shows a list of all runways in this analysis that would benefit from LAAS complex approaches: ALB 28, BDL 15, BHM 18, BHM 36, BUR 15, DCA 19, HNL 22L, HNL 26L, HNL 26R, JNU 8, JNU 26, LGA 31, SAN 27, and TEB 01.

### Methodology

A key assumption in this methodology is the decision height achievable by LAAS complex approaches at these runways.  Since MITRE’s GAME model provides estimates of decision heights for straight-in approaches, its output can be used to inform us that these runways are obstacle constrained to relatively high decision heights.  In this analysis it was assumed that there will be a learning curve (or period of becoming comfortable with) for advanced capabilities such as these complex procedures.  Most newly introduced technologies do not achieve the full potential of their capabilities until users become familiar with, and comfortable with, those capabilities.  Thus, it is assumed that during the early years that a LAAS is used at each airport, the decision height for a complex approach is no better than that associated with straight-in approaches. Then, beginning in 2018, it is simply assumed that a complex terminal area path can be designed to support the full Cat I decision height (200 feet), and that Cat II/III minima are also achievable.  Since it is not known whether a complex path can be constructed at each of these runways to achieve these minima, it is recognized that this may be an aggressive assumption.

These assumed decision heights are then used as inputs to the method described in the section titled “Reduced Disruptions for Straight-in Precision Approaches”.  As in that section, the numbers of reduced disruptions due to the improvement in approach minima are estimated.  Other benefits often associated with complex procedures, such as reduced time or distance through the terminal airspace, appear to be attributable to RNAV or RNP procedures, and the role of LAAS in achieving these benefits is unclear.

### Limitations

For some runways included in this complex benefit estimate, it may be possible to install an ILS.  Installation of an ILS would change the baseline against which LAAS is evaluated, and that runway’s incremental LAAS-based complex approach benefit would be eliminated.  Efforts to obtain data on ILS siting potential at NAS runways have not yet been fruitful.

The complete solution to the question of LAAS complex approaches involves significant complex technical issues beyond the scope of this study.  This method assumes that the complex approach segment has allowed the aircraft to avoid controlling obstacles and intercept the final approach path at a point closer to the runway than current procedures. A preliminary evaluation of decision height improvements due to short finals, conducted by CAASD using the GAME tool, and based on GLS TERPS, indicated that few, if any, of the 121 airports would achieve any decision height benefit from such short finals. The impact of possible future changes in TERPS for LAAS approaches on achievable decision height for short final is unknown.

### Results

Tables 9A and 9B show the total LAAS complex approach benefit estimated for the 121 airports studied.  Table 9A shows these benefits for Cat I LAAS implementation, in terms of both reduced direct operating costs and passenger time savings, as well as for the two scenarios of user WAAS equipage.  Table 9B shows these benefits for Cat II/III LAAS implementation.  Total complex approach benefits are obtained by adding corresponding cells from Tables 9A and 9B (e.g., total DOC benefit for 0% WAAS is $ 101.5M = $95.5M + $6.0M)

Table 9a: Discounted 20 year LAAS Complex Approach Benefits for Cat I

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $95,500,000 | $109,800,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $0 | $0 |

Table 9b: Discounted 20 year LAAS Complex Approach Benefits for Cat II/III

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $6,000,000 | $7,500,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $6,000,000 | $7,500,000 |

## Benefits Due to Elimination of ILS Critical Areas

Under certain weather conditions, the ILS signal must be protected by ensuring that aircraft or other vehicles do not enter areas on the airport surface where they may interfere with the ILS signal quality.  These areas are called ILS critical areas, and are shown on taxiway diagrams, and are marked with appropriate signage on the airport surface. These critical areas require that aircraft taxiing into position for takeoff, or to cross the runway, must hold short at some distance from the runway.  The critical area is protected when instrument approaches are being conducted with visibility less than or equal to 2 miles or ceilings less than or equal to 800 feet.  Figure 3 illustrates an ILS critical area on Cincinnati’s runway 18L.

Figure 3. Example of an ILS Critical Area hold.

Protection of ILS critical areas may cause delays to both the arriving aircraft, and to aircraft taxiing on the airport surface.  The impact that LAAS may have on each of these delays is explored in the following sections.

### Arrival Delay due to Protection of ILS Critical Areas

When arrival and departure operations are being conducted during the same period on a single runway with an ILS critical area, the arriving aircraft must be spaced further apart longitudinally in order to allow for the time required for the departing aircraft to taxi through the critical area and onto the active runway.  This results in a reduced rate of operations on that runway.

LAAS, when used for precision landing guidance in IMC, is expected to eliminate the need for ILS critical areas on the airport surface.  With departing aircraft able to taxi closer to the runway, less time is required for their final taxi into position for takeoff, with a resulting reduction in required longitudinal spacing between sequential arrivals as well as between arrivals and departures.  Thus, the elimination of ILS critical areas should allow a higher pace of operations on these runways where both arrival and departure operations are being conducted during reduced weather minimums.  Based on input from airline representatives, actual GPS approach minima were used as a baseline.  In the absence of actual GPS approach minima, RNP-0.3 minima from the GAME model were used. The purpose of this section is to estimate the impact that ILS critical areas have on airport capacity and average arrival delays.

The following is the methodology that was used in this analysis.

### Methodology

- Identify ILS critical areas within the 121 studied airports

- Identify which of the runways associated with these critical areas are used for both arrivals and departures during IMC

- Calculate the estimated time in seconds to taxi through each critical area

- Determine the minimum required aircraft time separation at the runway threshold, for two cases:

  - No critical area: Separation is dictated by wake vortex separation standards

  - ILS critical area: Separation between affected arriving aircraft is increased by the time needed for the departing aircraft to taxi through the critical area

- Convert the minimum aircraft time separation into a runway capacity per hour for each case

- Calculate the percentage of time that weather is between LAAS minima and baseline minima

  - Use published minima associated with GPS procedures whenever available

  - In the absence of actual GPS minima, use GAME RNP-0.3 minima

- Use IBM’s Single Airport Delay Model to estimate the flight delays associated with each of these cases for a typical traffic volume day

- Take the difference in delays between these two cases to get the one-day delay savings for ILS critical area elimination

- Multiply by the percent of LAAS avionics equipage

- Multiply by the downstream effect factor (see Appendix N)

- Multiple by .999, the assumed availability of LAAS

- Annualize the one-day delay savings and multiply by the cost of airborne delay for each user group in $/min

### Limitations

ILS Critical Areas were identified from airport taxiway diagrams.  ILS Critical Areas that are not identified on the taxiway diagrams (e.g., ILS critical area between SEA 16R and 16L, identified by SEA airport and airline representatives), and where runway operations include IMC arrivals and departures, are not included and may provide additional potential benefits.

### Example: Cincinnati Airport (CVG)

Typical runway configurations at CVG include departures on runway 27, and both departures and arrivals on either 18L/R or 36L/R, depending on wind conditions. CVG has an ILS critical area hold on every runway.  Since runway 27 is dedicated to departures, it was assumed that most departures will be sent to this runway, with only those departures above and beyond the capacity of runway 27 being sent to the other runways.  The OAG schedule data show that the IMC departure capacity of runway 27 is exceeded 11 of the 16 hours between 6 a.m. and 9 p.m.  Thus, in IMC the demand that exceeds runway 27’s capacity (approximately 160 departures per day) must use either 18L/R or 36L/R, depending on wind direction.  It is these aircraft that are subject to hold at the ILS critical areas, and which will thus require greater spacing between arrivals in order to execute their departure.

Applying the steps of the methodology outlined above, it was found that CVG’s ILS critical areas require aircraft to taxi an additional 15 seconds when departing on runways 18R and 36L and 25 seconds when departing on runways 18L and 36R. This additional taxi time results in a ¾ mile increased separation between arrivals on runway 18R/36L, and 1¼ mile additional separation for 18L/36R.  Next, the change in arrival capacity represented by these increased arrival separations was calculated, and used to estimate changes in airport delays.  Finally, a total annual direct operating cost savings and passenger time savings due to reduced delays from ILS critical area elimination at CVG was calculated.  For CVG, discounted 20 year Cat I and Cat II/III benefits for the scenario in which no users equip with WAAS is $5.6M for DOC and $5.9M for PTS.  Discounted 20 year Cat I and Cat II/III benefit for the scenario in which all users equip with WAAS is $2.2M for DOC and $2.3M for PTS.

### Results

Tables 10A and 10B show the total LAAS ILS critical area arrival delay benefit estimated for the 121 airports studied.  Table 10A shows these benefits for Cat I LAAS implementation, in terms of both reduced direct operating costs and passenger time savings, as well as for the two scenarios of user WAAS equipage.  Table 10B shows these benefits for Cat II/III LAAS implementation.  Total benefits are obtained by adding corresponding cells from Tables 10A and 10B (e.g., total DOC benefit for 0% WAAS is $ 8.2M = $5.3M + $2.9M).

Table 10a: Discounted 20 year LAAS ILS Critical Area Arrival Delay Benefits for Cat I

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $5,300,000 | $5,600,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $900,000 | $900,000 |

Table 10b: Discounted 20 year LAAS ILS Critical Area Arrival Delay Benefits for Cat II/III

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $2,900,000 | $3,100,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $2,900,000 | $3,100,000 |

### Taxi Time Delay due to Protection of ILS Critical Areas

The elimination of an ILS critical area may allow for a less impeded flow of arrival and departure ground operations across runways that currently have critical areas requiring a hold. The purpose of this section is to estimate the impact that ILS critical areas have on aircraft taxi operations.

Since multiple factors affect the pace of ground operations, it is necessary to attempt to isolate the contribution to taxi time delay that comes from protection of the ILS critical areas.  Although the requirement to protect the critical area is limited to ceiling and visibility conditions below 800 feet or 2 miles, anecdotal evidence and interviews with industry representatives suggests that critical areas are sometimes protected even in conditions outside of these limits.  This practice complicates the process of isolating the operational impact of ILS critical area protection.

Observed taxi times were collected for each airport for weather conditions above and below the GPS minima (in absence of actual GPS minima, use GAME RNP .3 minima).  These actual taxi times were then compared to the unimpeded, or expected, taxi times.  For conditions at or below the GPS minima limits, the difference between these is simply the IMC taxi delay (observed time – expected time).  However, there are taxi delays even in VMC, so the calculated IMC taxi delay was normalized by removing this VMC delay.  The remaining IMC taxi delay should reflect conditions that are unique to the airport’s IMC operational conditions.  Subtracting all of the VMC taxi delay in the normalization step may be excessive, as there may be more volume related taxi delays in VMC than IMC.  However, taking this step suggests that the resulting estimate is conservative.  One final step, the subtraction of the normalized IMC delay averaged over all airports without an ILS critical area (34 of 121 airports studied have a critical area hold, consisting of 91 total runways), should help to eliminate those delays attributable to weather and congestion, leaving delays due primarily to protection of ILS critical areas.

The following is the methodology that was employed in this analysis:

### Methodology

- Identify ILS critical areas within the 121 studied airports

- Identify the actual and unimpeded (expected) taxi-in and taxi-out times from the ASPM database

- Calculate the percentage of time that weather is between LAAS minima and baseline minima

  - Use Baseline GPS minima whenever possible

  - In the absence of actual GPS minima, use GAME RNP-0.3 minima

- Calculate a normalized average IMC taxi-in and taxi-out delay per flight that isolates the delay due to protection of ILS critical areas:

  - Obtain the raw IMC taxi time delay by subtracting the IMC unimpeded taxi time from the IMC observed taxi time

  - Obtain the raw VMC taxi time delay by subtracting the VMC unimpeded taxi time from the VMC observed taxi time

  - Obtain the normalized IMC taxi time delay by subtracting the raw VMC delay from raw IMC delay – this normalized IMC taxi delay represents delays in IMC, which may be due to both general operational slowdown in IMC and to protection of ILS critical areas

  - Further isolate the taxi delay specifically due to protection of critical areas by subtracting the average IMC taxi delay, normalized for VMC delay, observed at airports without critical areas

- Multiply this final normalized IMC taxi time delay, assumed to be due primarily to protection of ILS critical areas, by the cost of ground delay for each user group

- Adjust these delays for the percent of LAAS equipage

- Multiply by the downstream effect factor (see Appendix N)

- Multiply by .999, the assumed availability of LAAS

- Annualize the one-day delay savings and multiply by the cost of ground delay for each user group in $/min

Note that this methodology accounts for taxi delays associated with aircraft, but does not include restrictions on other types of airport surface traffic due to protection of ILS critical areas.

### Results

Tables 11A and 11B show the total LAAS benefits from the reduction in taxi times made possible with the elimination of ILS critical areas.  Table 11A shows these benefits for Cat I LAAS implementation, in terms of both reduced direct operating costs and passenger time savings, as well as for the two scenarios of user WAAS equipage.  Table 11B shows these benefits for Cat II/III LAAS implementation. Total taxi delay benefits are obtained by adding corresponding cells from Tables 11A and 11B (e.g., total DOC benefit for 0% WAAS is $ 27.9M = $17.6M + $10.3M)

Table 11a: Discounted 20 year LAAS ILS Critical Area Taxi-In and Taxi-Out Delay Benefits for Cat I

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $17,600,000 | $28,300,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $2,800,000 | $4,600,000 |

Table 11b: Discounted 20 year LAAS ILS Critical Area Taxi-In and Taxi-Out Delay Benefits for Cat II/III

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $10,300,000 | $16,600,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $10,300,000 | $16,600,000 |

## Benefits for Closely Spaced Parallel Approaches

During VMC, the FAA allows aircraft to conduct simultaneous independent approaches on parallel runways separated by as little as 700 feet as long as the pilots take over separation responsibility using “see and avoid” principles.

When weather deteriorates, maintaining visual separation is no longer possible and there are specific rules about the required separation between runways under which aircraft can conduct simultaneous independent parallel approaches.  Currently, the minimum required separation is 4300 feet in IMC (without special Air Traffic Control (ATC) radar surveillance equipment, called a Precision Runway Monitor (PRM)).  This separation is required to ensure adequate time to prevent a collision in the event that one of the aircraft on a parallel runway approach (the blundering aircraft) turns in the direction of the second aircraft (the evading aircraft).  The separation distance is a function of the surveillance error, navigation system error, flight technical error, and the time required to detect the blunder, alert the evading aircraft, and conduct an evasive maneuver.

With improved surveillance, pilot and controller training, and special procedures, it is possible to conduct simultaneous independent parallel approaches down to as little as 3000 feet runway centerline separations.  This entails the use of PRM, a high update radar and high resolution display, which can cost more than $10M per unit.  Currently, if the runway centerlines are separated between 2500 and 3000 feet, the approaches must be dependent with the aircraft positioned so as to have a minimum 1.5 nautical mile stagger on the parallel runways.  For runways separated by less than 2500 feet, neither independent nor dependent approaches can be conducted in IMC due to the potential hazardous effects of wake vortices, and consequently one of the parallel runways is shut down for arrivals.

### Evidence in Support of Potential LAAS Benefits

Given that the separation distances are based in part on navigation system errors, it seems logical to assume that it may be possible to achieve reductions in the required separations distances (i.e., below 4300 feet) with new navigation systems such as WAAS and LAAS.

In fact, a number of research efforts have been conducted on this issue as well as a host of other technical issues related to achieving increased airport capacity through a reduction in runway separations.  These research efforts have included:

- Various studies by Sharon Houck and her colleagues at Stanford University, showing the feasibility and potential benefits of WAAS or LAAS combined with tunnel-in-the-sky displays to reduce runway spacing while maintaining currently accepted safety levels.

- NASA’s Terminal Area Productivity Program which includes the Airborne Information for Lateral Spacing (AILS) and the Closely Spaced Parallel Approach (CSPA) Program.  As part of this effort, NASA has been investigating ways to mitigate the effects of wake vortices on closely spaced parallel approaches.

- Investigations of parallel runway technical issues and air traffic control procedures conducted by RTCA SC-186, Working Group 1.

- Studies by Eurocontrol of the benefits of the Ground Based Augmentation System (GBAS), including studies specific to simultaneous independent operations.

- Massachusetts Institute of Technology (MIT) Lincoln Lab analyses and tests of PRM and associated procedures.

- Analyses by MITRE/CAASD over the past 20 years supporting the FAA’s research, feasibility studies, and certification of various simultaneous independent parallel approach procedures (including most recently, the RNP Parallel Approach Transition or RPAT) as well as investigating reductions in wake turbulence constraints.

It is clear from these studies that the largest contributor to the required separation between parallel runways is surveillance error, flight technical error, and the distance needed to detect and resolve potential blunders.  Although navigation system errors are not insignificant, their contribution to the required runway separation is minor (i.e., less than 20% of the 4300’ separation requirement) compared to other errors and required distances.

Without new technologies to reduce the size of the surveillance errors and flight technical errors as well as automated methods for detecting and resolving blunders, LAAS alone is likely to have a negligible impact on the reduction of lateral separations required for simultaneous independent parallel approaches.

Nevertheless, the existing studies indicate that LAAS can be combined with other technologies such as a tunnel-in-the-sky display or Automated Dependent Surveillance-Broadcast (ADS-B) and Cockpit Display of Traffic Information (CDTI) to enable those technologies to achieve performances that they would not be able to attain without LAAS.  For example, Houck et al. illustrated that a tunnel-in-the-sky display in the cockpit combined with linear instrument approach corridors made possible with WAAS can result in reductions in the required separation between parallel runways from 4300 feet to 3100 feet.  Clearly, with the greater horizontal and vertical accuracy of LAAS when compared to WAAS, it should be possible for LAAS to achieve and possibly surpass the reduction to 3100 feet estimated to be attainable with WAAS.

Although not explicitly tied to LAAS, the FAA’s Safe Flight 21 program indicates that ADS-B could provide PRM-like capability at a wider range of airports. Since the utility of ADS-B is linked to the accuracy and availability of its inputs, utilizing the best available positioning information (i.e., LAAS, where available) will maximize ADS-B’s value.  The FAA is also exploring the use of RPAT (an ILS approach path on one track combined with an RNP approach procedure and a visual guided side step maneuver on the parallel track) for use with closely spaced parallel runways.  The possibility of using LAAS to increase the usability of RPAT procedures appears to hold some promise, but is a research topic outside of the scope of this benefits analysis.

Given the uncertainty associated with the procedures and additional technologies that will be required to support simultaneous independent parallel approaches in Cat II/III conditions in combination with LAAS, IBM chose not to quantify the potential LAAS benefits from such an application.  Any benefits that might be achievable for simultaneous independent parallel approaches in Cat II/III conditions would be in addition to those stated in this report.

In the following analysis, the potential improvement that may be achieved when LAAS is combined with improved cockpit displays was estimated for both the 0% and 100% WAAS user equipage scenarios.  For the 100% WAAS equipage case the incremental accuracy of LAAS over WAAS is not expected to produce an appreciable difference in the required runway centerline separation requirement for simultaneous independent parallel approaches, and LAAS accrues benefits for the years prior to WAAS Cat I capability in 2015.

There are 12 airports among the 121 candidate airports in the LAAS benefits analysis that would be affected if the required separation for simultaneous independent parallel approaches were reduced from 4300 feet to 3100 feet. They include:

- Detroit (DTW)		(    Memphis (MEM)			(    Portland (PDX)

- Ft. Lauderdale (FLL)		(    Milwaukee (MKE)		(    Raleigh-Durham (RDU)

- Jackson (JAN) 		(    Minneapolis-St. Paul (MSP)	(    Salt Lake City (SLC)

- Long Beach (LGB)		(    New York – Kennedy (JFK)	(    Tampa (TPA)

Minneapolis-St. Paul already has a PRM and thus is unlikely to benefit from a combination of LAAS and other technologies and therefore it was excluded from the analysis.  Ft. Lauderdale, Salt Lake City, Memphis, and New York - Kennedy, are listed in the Aviation Capacity Enhancement (ACE) Plan as sites recommended for a PRM.  It is possible that these airports may be too far along the procurement path to have LAAS make a difference.  However, since delays in implementation may still occur, it was decided to include these airports in the analysis.  The remaining airports (Tampa, Detroit, Milwaukee, Jackson, Raleigh-Durham, Long Beach, and Portland) are not in the list of sites recommended for a PRM, and may be candidates for a capacity improvement with LAAS.

Using capacities from the FAA benchmark report and FAA’s ASD organization, an estimate was obtained of the impact that bad weather has on these airports and the magnitude of the potential arrival capacity gains that may be achieved if the capacity from the parallel runways at these airports is partly or wholly regained with LAAS and associated technologies.  Note that these capacity gains are due to the availability of runways that would otherwise be closed due to insufficient runway separation or to runway pairs that would be reduced to conducting dependent approaches.  Thus, these gains are above and beyond those calculated in the straight-in analysis described earlier in this report.  Table 12 contains a list of the 11 airports that were part of this analysis and their capacities. Note that the capacity reduction at these airports ranges from 14% at Detroit to a high of 67% at Long Beach.  A reduction of over 50% is probably caused by the closing of one of the two parallel runways whereas a more limited reduction in capacity (e.g., 32% at MEM) is likely to indicate the use of dependent parallel approaches at the airport when the weather deteriorates.

Table 12.  Capacities of Airports with Parallel Runways Between 3100 and 4300 ft. Separations Between Centerlines (Excluding MSP)

| Airport ID | Airport Name | Optimum Hourly Arrival Capacity | Reduced Hourly Arrival Capacity | % Arrival Capacity Reduction |
| --- | --- | --- | --- | --- |
| DTW | Detroit | 84 | 72 | 14 |
| FLL | Ft. Lauderdale | 65 | 27 | 58 |
| JAN | Jackson | 60 | 40 | 33 |
| JFK | New York- Kennedy | 74 | 48 | 35 |
| LGB | Long Beach | 70 | 23 | 67 |
| MEM | Memphis | 88 | 60 | 32 |
| MKE | Milwaukee | 72 | 34 | 53 |
| PDX | Portland | 60 | 38 | 37 |
| RDU | Raleigh-Durham | 60 | 40 | 33 |
| SLC | Salt Lake City | 90 | 40 | 56 |
| TPA | Tampa | 71 | 50 | 30 |

### Methodology

In order to describe the methodology employed in this analysis, an example involving JFK is described.  To determine the impact that a capacity reduction of the size shown in Table 12 can have on congestion and delays, the IBM Single Airport Delay Model was applied to the demand and capacity data.  The arrivals for a representative traffic day were compared to the optimum and reduced capacities at JFK.  This analysis focused on Cat I operations, although there is no restriction preventing Cat II/III simultaneous parallel operations on runways separated by 3400 feet.  Since reduced capacity conditions occur approximately 7.5% of the time at JFK, or on average about 1.75 hours per day, a moving window of reduced delay was applied to the model, effectively creating different scenarios representing many possible combinations of 1.75 hour windows during the course of a day.  For each of these scenarios, the average daily delay was calculated. A total average delay was then calculated across the scenarios. This model result (0.03 minutes per flight) was compared to the total average delay obtained with JFK at optimum capacity (0.0 minutes per flight).  The difference in delays, 0.03 minutes per flight, represents the potential improvement that can be achieved with LAAS.

Multiplying this value by the number of flights by user group yields the delay minutes by user group. Then, multiplying by the cost of a minute of airborne delay yields the total cost savings that might be achieved at JFK.  Finally, recognizing the fact that LAAS will need to be combined with other technologies to achieve this benefit, a factor of ½ was applied to the result.  As with the other benefits estimated in this report, a downstream effect factor (see Appendix N) was applied, as well as an availability factor of .999, the assumed availability of LAAS.  Over the 20 year benefits period, the total direct operating cost savings for the 0% WAAS equipage scenario at JFK is estimated to be $259,000.

### Results

Table 13 shows the LAAS closely spaced parallel approach benefit for Cat I LAAS implementation, in terms of both reduced direct operating costs and passenger time savings, as well as for the two scenarios of user WAAS equipage.

Table 13: Discounted 20 year LAAS Closely Spaced Parallel Approach Benefits for Cat I

|  | Direct Operating Cost | Passenger Time Savings |
| --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $9,900,000 | $10,600,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $200,000 | $0 |

As indicated above, LAAS without advanced cockpit technologies or LAAS in the presence of a 100% WAAS equipage scenario is unlikely to lead to a significant reduction in runway separation distances required to conduct simultaneous independent parallel approaches.  However, evidence from previous studies seems to support the conclusion that LAAS, when combined with other advanced avionics, may be able to reduce these distances and result in sizable quantifiable benefits in the 0% WAAS equipage scenario.  This comes about from the combination of improved navigation system accuracy and reduction in the flight technical error.  LAAS may also enable more accurate position reporting when used in concert with ADS-B, thus reducing the surveillance error.  This may lead to additional reductions in the required separation distances between runway centerlines.

## Qualitative Efficiency Benefits

Several sources of potential efficiency benefits were evaluated qualitatively, including variable glideslopes, data uplink, airspace conflict resolution, missed approach guidance, and surface navigation.  Each of these may prove to be an important source of benefits from LAAS implementation.  However, these sources were not considered for quantitative estimation for several reasons, including the speculative nature of such benefits, particularly the significant uncertainties about the timing of implementation of such capabilities, and the considerable changes to current operating procedures required to obtain these benefits.  Additionally, the lack of relevant data on current operations places severe limits on the ability to quantify these benefits.

### Benefits From Variable Glideslopes

The ability of LAAS to support multiple simultaneous glideslopes (separate vertical paths, each at a unique vertical angle, and each capable of providing precision vertical guidance for aircraft during approach and landing) may provide a level of flexibility not available with the current precision approach infrastructure. In addition to the possibility of allowing various vertical angles, these independent glideslopes may lead either to the same or to different touchdown points on the same runway.  This capability also opens the possibility of providing temporary changes in precision approach paths (e.g., to accommodate runway construction) more readily than is possible with an ILS.

Specific examples of potential benefits include:

- EWR runway 11 – Continued operations via steeper glideslope during times when harbor cargo ships interfere with current fixed ILS glideslope angle.

- MEM runway 17/35 – Temporary approaches used during runway construction.

- Decreased longitudinal spacing between aircraft by placing lighter aircraft on a steeper glideslope than heavy aircraft, in order to avoid wake vortex problems (as shown in Figure 5B).

### Figure 5. Illustrations of Potential Benefits: A) Multiple Glideslopes, Same Touchdown Point and B) Multiple Glideslopes, Different Touchdown Points

### Limitations

- The range of practical glideslope angles is limited by aircraft performance characteristics, and therefore not all current limitations will be addressable.

- Temporary approaches would still have to be flight tested and the displaced threshold may not accommodate all aircraft due to the shortened runway length.

### Benefits from Digital Data Uplink

The uplinking of data, including RNAV and precision approach path waypoints, may provide a level of flexibility for air traffic operations in the terminal area not available with the current precision approach infrastructure.  The ability for the service provider to dynamically alter the paths taken by individual aircraft in the terminal area, while positive guidance is maintained in the cockpit, would represent a significant change in air traffic operations.  The uplink of path segments (e.g., (Standard Instrument Departure Procedures) SIDs and Standard Terminal Arrival Route  (STARs)) using LAAS may have some benefits, but at this time the technical and procedural details of this capability have not been fully established, and a number of issues have been identified, including:

- The need for software in the cockpit to convert waypoint data in the ARINC 424 format to that used by the FMS and/or multimode receiver (MMR). This software may result in substantial additional costs and probably would require recertification of the existing avionics.

- The waypoint data for approaches (STARs) would have to be uplinked when the aircraft is still in the cruise stage or just beginning its descent at a point approximately 100 nautical miles from the airport.  That would mean that the current service volume for LAAS Cat I operations of approximately 20 nm would have to be extended an additional 80 nm to support this activity.  Obviously, this would introduce a host of major issues.

- Every change in a SID or STAR would require flight checking the LAAS transmission, according to FAA regulations.

- The uplinking of SID or STAR data would require replacing data in the FMS, possibly with pilot oversight.  It is unclear what the role of the pilot would be in this process.  New procedures would have to be defined.

- There may not be sufficient channel capacity to support the uplinking of SID and STAR data (since these messages tend to be very complex), particularly if multiple segments need to be transmitted to provide an alternative plan in case of an emergency.

- If the SID or STAR is uplinked directly to an MMR, there will be a requirement for a new cockpit display to visualize the trajectory.  Such a display would take years to develop and certify.

If these issues are resolved, and procedures are developed to take advantage of the flexibility provided by the LAAS data uplink, this capability may provide important benefits for both operators and service providers.

### Benefits from Airspace Confliction Resolution

The horizontal and vertical accuracy of LAAS, whether as precision guidance system, or in support of RNAV/RNP procedures, may provide the capability to resolve conflicts in airspace usage among adjacent airports and between arrivals and departures at the same airport.  The capability to resolve airspace conflicts may reduce the airspace needed per operation, thus allowing a greater density of operations in a given airspace.  This capability may be of particular importance in highly congested airspace (e.g., the Chicago, New York, and Los Angeles areas).

The following airports were cited by airline and airport representatives as examples of locations where this benefit could be applied.

- SEA			SEA may be able to increase efficiency by separating arrival and

departure streams.

- BFI 			BFI arrivals conflict with SEA operations during north flow operations.

- MDW 			MDW 13C arrivals conflict with ORD 22L departures and 14L arrivals.

- PWK			PWK 34 circling arrivals conflict with ORD 32R departures.

- HOU 			Conflict with IAH traffic

- FLL 			Conflict with MIA traffic

- BUR 			Conflict with LAX traffic

- JFK-LGA-EWR-TEB Significant conflicts among these airports, depending on wind and

weather conditions.

### Limitations

- Each airspace environment is unique and must be evaluated thoroughly to identify how, and under what circumstances, LAAS may contribute to airspace conflict resolution.  It is expected that only the most complex and congested airspace environments will require a LAAS-based solution.

- Some airspace conflict resolution may be possible with RNAV capabilities through the use of GPS and/or WAAS.  In these cases, LAAS may show little to no benefit.

### Benefits from Guided Missed Approach

LAAS may have the capability to provide precision guidance, potentially including complex or curved paths, for the missed approach segment.  A low-RNP and/or complex guided missed approach may permit reductions in approach minima and/or continued use of one or more runways during low weather minima conditions.  Figure 6 below shows an example of a hypothetical precision guided missed approach for ORD and SEA.

| ORD In order to maintain approaches to 9R/9L and 4R, ORD would benefit from the ability to have precision guided, curved missed approaches. | SEA A precision guided, curved missed approach would allow for increased arrival throughput to 16R, since arriving aircraft would not have to wait for 16L Departures. |
| --- | --- |

### Figure 6. Illustrations of Potential Benefits at Chicago O’Hare (ORD) and Seattle (SEA)

### Limitations

- Some of these benefits may be achievable with RNAV capabilities through the use of GPS and/or WAAS.  In these cases, LAAS may show little to no benefit.

- No data exists at this time to determine the lower approach minima that may be associated with low-RNP and/or complex guided missed approach procedures.

### Benefits from Precision Guided Surface Navigation

Precision guidance for surface navigation operations would give both ground controllers and pilots greater situational awareness, particularly at night and under low visibility conditions.  This precision guidance may help reduce ground delays (e.g., delays caused by aircraft and surface vehicle interactions, delays caused by aircraft running off taxiways, delays caused by using an incorrect taxiway at night). LAAS, used with enabling technologies such as ADS-B, moving map, and CDTI, may contribute to achieving precision guidance for surface navigation.

Potential Benefit Examples

- Reduce delays from reduced:

  - incidents of aircraft running off taxiways  (e.g., the new Airbus 380 has an unusually wide track which may limit access to many airports’ taxiways).

  - incidents when aircraft inadvertently use taxiways for takeoff

  - incursions between airport ground vehicles and taxiing aircraft

Examples of Airport Surface Incidents That May Have Benefited from Precision Guided Surface Navigation:

- Aircraft ran off taxiway:

  - “March 25, 2001. USA, Maryland, Baltimore International Airport: a Southwest Airlines Boeing 737, flight 459 with 141 people on board ran off a taxiway while preparing for takeoff; no one was injured.”

  - “An aircraft has run off the taxiway at Birmingham International Airport causing diversions for other flights. The plane landed safely and was taxiing when its nose wheel came off the tarmac.”

- Aircraft used taxiway for takeoff:

  - "The captain's selection of a taxiway instead of a runway for takeoff and the flight crew's inadequate coordination of the departure, resulted in a departure from a taxiway. A factor in the incident was inadequate airline operator's procedures that did not require the crew to verbalize and verify the runway in use prior to takeoff."

- Ground vehicle causes incursion:

  - “An unidentified vehicle crossed ORD Runway 22R via Taxiway N without clearance. B737, over landing threshold for Runway 22R executed a go-around, flying directly over the vehicle. Vertical separation was 50-100 feet.”

### Limitations

- Use of LAAS for surface navigation will require the addition of some combination of enabling technologies, potentially including ADS-B, CDTI, and moving-map.

- Unless the horizontal accuracy (as well as availability, integrity, and continuity) provided by LAAS is shown to be exclusively required, GPS and/or WAAS may be an adequate alternative.

# Safety Benefits

This section presents a summary of methods and findings from the evaluation of potential LAAS safety benefits.  The full safety analysis report, from which this section is drawn, was produced by the Flight Safety Foundation (FSF), a recognized authority in the field of aviation safety analysis.  The full FSF report is available separately (Please refer to the FSF report, Safety Benefits of the

Local Area Augmentation System, for details).

Introduction

Currently, there are many different types of navigation-based approaches to runways at the more than 4,000 public use airports with paved runways. These airports have well over 10,000 runways, of which more than 1,150 have ILS precision approaches.  The remaining runways have no instrument approaches or use a variety of less precise non-precision instrument approaches.

A precision approach provides the pilot with both vertical and horizontal guidance to the end of the runway. The ability to maintain a constant reference to the vertical and horizontal path to the runway enhances the ability of a pilot to fly a stable approach. According to the Flight Safety Foundation, a stable approach is one where the aircraft is on the correct flight path, only small changes in heading and pitch are required to maintain that path, airspeed is at the correct approach speed, the aircraft is in the proper landing configuration, and the descent rate is a maximum of 1,000 feet per minute. In contrast, a non-precision approach provides the pilot with only horizontal guidance to the runway. The pilot is responsible for maintaining vertical separation from terrain using the aircraft’s altimeter and other onboard instruments. It is generally acknowledged that a precision approach is safer than a non-precision approach. This is supported by research conducted by the Flight Safety Foundation which indicated that the risk of an accident among air carrier airplanes is five times greater during a non-precision approach than a precision approach.

The GPS-based navigation system used for instrument approaches will ultimately provide some degree of precision instrument approach capability at many of the runways at the nation’s 4,000 public use airports. This is expected to have a profound and positive impact on aviation safety. The satellite-based navigation system has three main components: the GPS satellite constellation, and two augmentation systems, WAAS and LAAS.  WAAS currently provides multiple levels of navigation service across the NAS, including en-route, terminal, and approach guidance. WAAS is not expected to reach Category I approach standards (generally 200 feet ceiling and ½ mile visibility) until 2015. LAAS is expected to provide terminal area and approach guidance, particularly for the stringent requirements of Cat I, II and III approaches.  This paper addresses the anticipated safety benefits associated with LAAS.

The underlying hypothesis of this study is that LAAS will provide safety benefits attributable to a precision approach at runways without current precision approach service and when weather conditions are below those supported by systems in the baseline.  Consequently, any precision approach system (e.g, ILS, MLS, WAAS) should be capable of achieving the same benefits. The LAAS capabilities that are expected to lead to safety benefits include the following:

- LAAS will provide Category I approach capability at those locations where WAAS service is not anticipated or Category I ILS guidance is not provided.

- LAAS will provide Category II and Category III approach capability at facilities that do not currently have that capability.

- LAAS will provide positive surface guidance in reduced visibility, and/or in dark conditions, to aircraft equipped with HUD, LAAS, and the appropriate equipment to integrate the information.

- LAAS will provide positive three-dimensional navigational guidance in the cockpit that will reduce the risk of controlled flight into terrain (CFIT) accidents for approach and departure in the terminal area.

- LAAS will help reduce pilot and controller workload for complex approach and departure routings.

- LAAS will provide positive lead-in guidance to parallel approach situations.

To evaluate the safety benefits of LAAS implementation, the study relied heavily on a retrospective evaluation of accidents and incidents. The underlying rates of these accidents were used to project anticipated losses if LAAS were not implemented. Past studies and related literature were reviewed to ensure that all relevant references were considered as the data analysis proceeded. Once the benefits of LAAS implementation were determined, they were used to develop a cost assessment of the benefits of reduced crashes.

Methodology

The basic approach used for the analysis focused on the following steps:

- First, the actual crash and incident experience for the time period of 1993-2002 was reviewed and events were selected that might have been prevented if LAAS had been operational.

- Using this information, a baseline incident rate per 1,000,000 departures based on the 10 year period of 1993-2002 was developed.

- Next, the anticipated incident risk at the studied airports was estimated for the time period of 2009-2028. This estimate was adjusted for an anticipated LAAS implementation that accounted for a gradual implementation of LAAS in the NAS.

- In addition, the impact of WAAS on these benefits was estimated, assuming a WAAS GLS IOC in 2015.

Using this approach, an estimate of crash risk during the implementation cycle of LAAS was developed. The anticipated number of lives saved and crashes prevented due to the future implementation of LAAS was also estimated. Using the resulting values, the estimated benefit of the anticipated reduction of losses in future dollars was developed.

Study Population

The study focused on two different populations. These were the operational environment of Alaska and that of the continental United States, or CONUS. The analysis for each study population was conducted in the same way, although some underlying assumptions were different.

For Alaska, all aircraft types were considered in the analyses. This included air carrier aircraft, commuter aircraft, and general aviation aircraft. The evaluation of safety benefits associated with LAAS in the CONUS was limited to air carrier and GA aircraft typically operated by business and corporate operators. Examples of aircraft included in the corporate category were turbine powered passenger aircraft and heavy piston-powered twins such as Piper PA-31 Navaho or the Cessna 400 series aircraft (Cessna 404, 414, 421). Smaller general aviation aircraft were not included in the CONUS analysis.  The analyses for all types of aircraft considered the anticipated benefit of LAAS with and without WAAS equipage on the aircraft.

Data sources

A number of data sources were used for this analysis. The National Transportation Safety Board (NTSB) accident and incident investigation database was used to identify accidents and serious incidents. The FAA’s National Airspace Incidents Monitoring System (NAIMS) was used to identify surface-related incidents that did not result in an accident. This included events such as runway incursions and surface near-collisions. Airport activity data, both historical and forecast, were obtained from the FAA’s Office of Aviation Policy and Plans (APO) TAF. On-line databases were queried and forecast reports were referenced. In addition to analyzing the National Transportation Safety Board data, the Flight Safety Foundation conducted an exploratory search of a single year's worth of NASA's Aviation Safety Reporting System (ASRS) data to determine if these reports, voluntarily filed  by pilots, might shed information on the frequency and severity of hazardous incidents that do not result in accidents, but that nevertheless might benefit from LAAS.   Based on this initial search, it was determined that there appears to be some evidence that LAAS could have mitigated or averted a number of incidents.  However, the incidents described in ASRS reports are not verified or investigated beyond an expert analysis of the reporter’s written narrative. As such, it is impossible to guarantee their authenticity or accuracy. Collectively, the voluntary nature of the ASRS and the reporting biases nullify the statistical utility of the data. For this reason, IBM and FSF chose not to pursue a more detailed review of this data.

Case Selection

Past accidents and serious incidents were used to provide insight on the potential benefits of LAAS. NTSB accident records were reviewed to determine what accidents, if any, might have been prevented if LAAS had been present. The methodology followed is described below:

- Initial Record Filter: All NTSB accident records for the time period of 1993-2002 were selected and compiled in a database using SPSS software. Records were then selected for accidents that occurred within 10 miles of an airport, while on approach, in IFR conditions, or while on the airport surface. This required that airport identification be provided.

- Airport Filter: Once the above filtering was completed, only those events that occurred at the study airports were selected.

- Manual Review: The resulting records were then used to obtain NTSB “briefs” which provided summaries of pertinent information associated with the accident and the resulting investigation. These briefs were reviewed independently by two different aviation subject matter experts to determine each case’s suitability for inclusion in the study. The manual review focused on determining the safety benefits if LAAS had been present. The potential benefits that might be attributed to WAAS were not considered during this part of the analyses but were accounted for later in the evaluation.  Additionally, among CONUS events, the brief was reviewed to determine whether the accident involved an air carrier or corporate type of aircraft using make and model as the initial indicator. This was further confirmed by reviewing the narrative associated with the accident or incident as well as reviewing the regulation that the aircraft was operated under (FAR parts 121, or 135 or 91 for example).

Limitations of Quantitative Analyses

There are a number of limitations associated with this benefits evaluation. The applicability of a study such as this is directly related to the underlying assumptions. The discussion of the following limitations is designed to make sure that the reader is aware of some of the more notable limitations that could affect the results.

- Corporate Aircraft Activity Assumptions: For the analyses in this study, estimates for corporate aviation were derived by current and forecast activity statistics, reported by the NBAA in hours. These values were for the time period of 1997-2004 and indicated that 16.5% of all general aviation activity is conducted by corporate aircraft. The assumption that cannot be validated is that the ratio of corporate hours to all GA hours (16.5%) is the same for number of operations. If there is a bias, it will be consistent for both the reference period calculations as well as the forecast calculations, thereby minimizing the biasing effect of the error.

- Activity Forecasts: There are many factors that cannot be fully accounted for in generating long-range activity forecasts. Political events, economic dynamics, introduction of new technologies, and many other issues may result in actual activity levels that are smaller or greater than forecast. Since the activity estimates are used to derive event rates that are in turn used to generate estimates of actual events in the future, any errors in the activity measure may result in significant differences in the actual number of events that occur.

- Problem of Small Numbers: The type of events that were used in this analysis are relatively rare events. For example, for the time period of 1993-2002 there were an estimated 106.5 million departures that involved air carrier and corporate aircraft at the study airports in the CONUS. There were only 11 accidents, however, at these same airports for the same time period that might have been prevented with LAAS. Consequently, one additional event in which an air carrier crashed and killed all on board could have a profound effect on the resulting accident rates and future benefit projections. This problem does not invalidate the results, but needs to be considered since these events are rare.

- NTSB Screening Methods:  The methods chosen to conduct the initial computer screening of the NTSB accident records were somewhat conservative and may have missed relevant cases. The difficulty with this approach is that some NTSB records that were probably suitable for inclusion in the study, may not have been selected by the initial computer screening because of missing data in one or more relevant computer fields. The effect of potentially not including all relevant cases is to make the associated benefit assumptions more conservative, understating the potential benefit of LAAS.

Findings

Table 14 provides the distribution of approach and airport surface accidents in the CONUS stratified by aircraft category that would have been unlikely to have occurred if LAAS had been operational between 1993 and 2002 and the aircraft involved in the accident had been equipped with appropriate LAAS receivers.

Table 14: Distribution of Accidents in the CONUS That Would Have Benefited From LAAS, 1993-2002

| Category | Air Carrier Jet | Air Carrier Turbo-Prop | Corporate Jet | Corporate Turboprop | Corporate Heavy Piston Twin | Total |
| --- | --- | --- | --- | --- | --- | --- |
| Approach | 5 | 0 | 0 | 2 | 0 | 7 |
| Surface | 0 | 2 | 1 | 1 | 0 | 4 |
| Total | 5 | 2 | 1 | 3 | 0 | 11 |

While similar evaluation was attempted for the three airports in Alaska that were included in this analysis, no accidents were found that might have been prevented by the presence of a precision approach capability for the time period of 1993-2002. Consequently, the balance of findings presented in this section is limited to the CONUS.

Table 15 provides estimates of the future number of accidents with and without the precision approach capability provided by WAAS, or LAAS.  The majority of the estimated benefits are associated directly with the ability of LAAS to provide precision guidance service.  Other technologies exist which can also provide this service, including ILS.

Table 15: Number of Accidents With and Without LAAS and WAAS, 2009-2028

| Level of LAAS or WAAS Coverage | Projected Number of Approach Accidents 2009-2028 |
| --- | --- |
| With No LAAS or WAAS | 34 |
| With WAAS Only | 12 |
| With LAAS Only | 3 |

Tables 16, 17, and 18 provide a summary of the 20-year discounted LAAS safety benefits for precision approach and surface navigation.  All three tables show LAAS safety benefits for two WAAS equipage scenarios: with 100% WAAS equipage by operators, and with 0% WAAS equipage by operators.  The estimated precision approach benefits of LAAS, for the scenario in which operators do not equip with WAAS, total $38.1 million for the timeframe of 2009-2028 at the 117 study airports in the CONUS. For the scenario in which operators equip with WAAS, LAAS benefits were estimated to be $14.9 million.  Surface navigation benefits for LAAS are most likely shared with some enabling technology, like ADS-B, or moving map. To reflect this discrepancy, the benefits calculated by FSF were divided by two for this report. The estimated surface guidance benefits of LAAS with 0% WAAS equipage is $20.2 million for the time frame of 2009 to 2028 at the CONUS airports. Additionally, although FSF finds that LAAS is the most likely system to provide surface navigation positioning information, other systems, like WAAS or multilateration, may also be able to provide this service.  Therefore, the LAAS surface navigation benefit reported here for the 100% WAAS equipage scenario is zero.

Table  16: Discounted 20-Year LAAS Safety Precision Approach Benefits

|  | Accidents Prevented (Hull loss and damage) | Fatal Injuries Prevented | Serious Injuries Prevented | Total |
| --- | --- | --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $37,569,000 | $0 | $555,000 | $38,124,000 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $14,636,000 | $0 | $240,000 | $14,876,000 |

Table  17: Discounted 20-Year LAAS Safety Surface Guidance Benefits

|  | Accidents Prevented (Hull loss and damage) | Fatal Injuries Prevented | Serious Injuries Prevented | Total |
| --- | --- | --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $5,122,000 | $14,634,000 | $419,500 | $20,175,500 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $0 | $0 | $0 | $0 |

Table  18:  Discounted 20-Year LAAS Safety-Related Monetary Benefits (Precision Approaches and Surface Guidance)

|  | Accidents Prevented (Hull loss and damage) | Fatal Injuries Prevented | Serious Injuries Prevented | Total |
| --- | --- | --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $42,691,000 | $14,634,000 | $974,500 | $58,299,500 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $14,636,000, | $0 | $240,000 | $14,876,000 |

# Societal Benefits

In addition to efficiency and safety benefits, other benefits may exist which provide positive impact for society as a whole.  The following societal benefit areas have been investigated:

- Continuation of U.S. Technology Leadership in Air Navigation

- International LGF and LAAS Avionics Sales Revenue to U.S. Manufacturers

- Noise Abatement and Mitigation

- Reduced Impact on Environmentally Sensitive Areas

- LAAS as a Complement to Homeland Security

- LAAS and JPALS Providing Civilian and Military Compatibility

- Expansion of Air Commerce to Smaller Communities

- Increased Reliability of Air Service

Quantitative Analyses

IBM has investigated the potential quantitative LAAS Benefits that may be obtained through (1) sales of LGF and LAAS avionics to international airports and airlines, and (2) increased U.S. Airport Improvement Program and U.S airline revenue through a 1% increased load factor on 1% of operations.  These quantitative societal benefits are highly speculative, and are included only to illustrate the importance of the economic impact LAAS may provide.  These benefits estimates will not be incorporated in the total benefits derived from the efficiency and safety benefits analyses.

Qualitative Descriptions

Many of these qualitative potential benefits may also be achieved through current or emerging procedures (e.g., RNAV/RNP) or technologies (e.g., WAAS).  Therefore, further investigation should be considered to determine if, and by how much, LAAS may uniquely provide these benefits.

## Continuation of U.S. technology leadership in air navigation

In a recent speech, the Secretary of Transportation said, “Today, new aviation initiatives are underway in Europe and elsewhere. We are being challenged in manufacturing and in satellite positioning and navigation services as Europe develops the Galileo system, an alternative to our own Global Positioning System. We can work with our international partners to develop an interoperable aviation system that increases mobility.  Or we can refuse to engage, refuse to lead, and thereby let others set the rules of the world’s skyways.  We must not let that happen. If America wants to retain its global air transportation leadership, we need to modernize and transform our air transportation system – starting right now.  With the forthcoming modernization of GPS, satellite navigation will be far more important to aviation than it is today.”  LAAS could be an integral part of this modernization.

The FAA’s Flight Plan 2004-2008 specifically identifies GNSS augmentation systems as one tool to help reach the goal of “seamless operations around the globe…”, and advocates that the agency promote the “commercial proliferation, interoperability and use” of these systems.  The U.S. has historically taken a lead role in promoting satellite navigation around the world as the standard for 21st Century air navigation. As part of this standardization, the LAAS architecture was successfully presented and approved by the International Civil Aviation Organization (ICAO) Global Navigation Satellite System (GNSS) Panel in February 1997.  LAAS is an element in the full realization of benefits from investment in satellite navigation programs.  Further, despite its inherently local nature, LAAS can be a truly global navigation solution.  A LAAS installation outside of the U.S. can provide the same types of benefits as a domestic installation.  In this context, LAAS can be used to support the FAA’s international leadership goal, stated in the 2004-2008 Flight Plan, to “Promote seamless operations around the globe…”

The U.S. has the world’s most complex airspace and leads the world in the development of the new CNS-ATM (Communication, Navigation, Surveillance/Air Traffic Management) suite of technologies and operational concepts. The U.S. was directly involved in the development of ICAO’s Standards and Recommended Practices (SARPS) for the development of space-based and ground-based (SBAS/ GBAS) augmentation systems and GNSS, which became effective in November 2001. LAAS implementation may encourage a single standard for terminal area navigation globally. International implementation of LAAS could bring high-precision navigation service to areas now served by minimal or outdated equipment, allowing expansion of reliable air service by both U.S. and foreign carriers.

## International LGF and LAAS Avionics Sales Revenue

Overview

Our discussions with U.S. carriers revealed two important goals: 1) to simplify the number and variety of landing systems and procedures currently in use, and 2) to operate globally with the same set of simplified systems and procedures.  A single navigation and landing system, capable of global implementation, can contribute to achieving these goals.  If domestic carriers equip with LAAS, they will want to use this capability throughout their networks, including at overseas airports.  Therefore, IBM explored the potential market for international LGF sales.

Similarly, if domestic carriers equip with LAAS, foreign carriers operating to the U.S. will have an incentive to also equip with LAAS.  Therefore, IBM explored the potential market for international (Part 129) avionics sales.  Retrofit sales revenue was not included.

A detailed analysis of the possible extent of international sales would be a significant undertaking, and is out of the scope of this project.  Instead, the market size and potential benefit of international sales of both LGFs and LAAS avionics were estimated.

Methodology

- Revenue from LGF Purchase and Install

  - Estimate LGF purchase sales price: $600K purchase

Note: LGF installation cost is not included

  - Estimate the number of international airports served by U.S. carriers: 182

  - Estimate the number of international airports with current or planned MLS installations: 12 (plus 13 potential orders)

  - The potential international LGF market is (2) minus (3)

  - The maximum potential LGF benefit is (4) times $600K

- Revenue from LAAS Avionics

  - Estimate LAAS avionics sales price: $10K

Note: Any potential LAAS retrofit sales are not included

  - Estimate the number of international carriers’ aircraft serving the 121 studied airports: 846

Note: Assume international carriers will equip all aircraft that serve the U.S.

  - The maximum potential LAAS avionics benefit is (2) times $10K

Results:  Market Estimate and Maximum Potential Original Equipment Manufacturer (OEM) Benefit

- International LGF

  - Market Estimate is 157 airports

  - Maximum Potential OEM Benefit is $94,200,000

- International (Part 129) Avionics

  - Market Estimate is 846

  - Maximum Potential OEM Benefit is $8,460,000

## Noise Abatement and Mitigation

While many airports seek to expand their facilities and operations to serve current and expected future demand for air travel, the communities surrounding airports also continue to expand, filling previously unused land in the vicinity of the airports. One result is a growing concern about aviation-related noise and its impact on these communities. Airlines and airframe manufacturers have worked together to significantly reduce the noise produced by modern aircraft, but noise generation remains a problem for many airports. More precise navigation in the terminal area may offer an opportunity to greatly reduce the impact of aviation-related noise by restricting aircraft to defined three dimensional routes designed to reduce the noise effects.

Through the flexibility offered by LAAS to construct complex, defined, highly repeatable flight paths that can be used during all weather conditions, the current costs associated with noise mitigation and noise abatement may be reduced. This section identifies the LAAS capabilities that can support noise reduction efforts, and summarizes some of the current costs associated with noise reduction programs.

Noise abatement and mitigation may be possible with RNAV capabilities through the use of GPS and/or WAAS.  In these cases, LAAS may show little to no benefit to enabling noise abatement and mitigation.

The FAA describes how aviation-related noise is measured as part of its Airport Noise Compatibility Program, found in Part 150 of the Federal Aviation Regulations.  These guidelines describe the noise levels that are considered acceptable and the impact that noise has on individuals and communities.

### Methodology

- Identify LAAS capabilities that may offer control over the generation and distribution of noise

- Review historical costs associated with airport noise

- Identify and group costs in one of the following areas where LAAS may provide potential reduction in:

  - Noise Program Costs

  - Noise Violations Cost

  - Land Acquisition for Noise Compatibility

  - Residential Home Soundproofing

  - School Soundproofing

  - Litigation

  - Airport Curfews

### Relevant LAAS Capabilities

The LAAS capabilities that may have a direct impact on noise issues are those that offer increased control over the flight path taken.  The ability to consistently provide defined, repeatable (laterally and vertically contained) flight tracks during all weather conditions allows for greater control over noise distribution and can offer potential cost savings for noise related programs and issues.

- Defined, repeatable flight paths: By defining a specific flight path that can realistically be expected to be repeatable, even in the busiest, most complex airspaces, LAAS-based procedures provide a way for airports and communities to achieve a balance that optimizes terminal area efficiency and reduced noise impact. Demonstration to community members of the high degree of three-dimensional repeatability of these paths, particularly compared to today’s wide range of flight paths taken could greatly reduce the time and costs typically associated with litigation over airport changes, such as runway expansions or additions.  Further, the reduction in flight path variability due to LAAS-based procedures may result in fewer homes and schools needing soundproofing, as well as reducing airport land acquisition costs.  See Figure 7 for an example of a defined, repeatable flight path.

- All-weather complex approach and departure procedures: Use of LAAS may allow aircraft to follow complex, noise mitigating, approach and departure routes during all weather conditions, including conditions of low weather minima. Other systems in the baseline that also support complex routes do not support operations to Cat II or III conditions.  Use of LAAS-based procedures assures that the same flight path is taken during all weather conditions, further reducing flight path variability as a function of weather.

Figure 7: Defined, repeatable flight paths through lateral and vertical containment

### Costs of Noise Abatement and Mitigation

The following summary provides examples of aviation noise related costs that LAAS capabilities may be able to reduce.  Costs incurred by airports are currently funded primarily through the Airport Improvement Program (AIP), the Passenger Facility Charge (PFC), as well as other federal, state, and local funds.

- Examples of Noise Abatement Program Costs

- Nationwide - $307 Million for airport noise pollution program

- MSP - $120M-$150M on noise abatement program

- ORD/MDW - $300M to reduce the impacts of aircraft noise on communities

- Examples of Noise Rule Violations Costs

- DEN: Violations of noise levels at DEN are subject to $500,000 per violation

- BOS: Penalties for violation of takeoffs on 4L above 73dBA and landings on 22R above 78dBA are fines ranging between $50 and $500 per offense

- Examples of AIP Funded Land Acquisition and Relocation Assistance for Noise Compatibility

According to the U.S. GAO, more than 75 percent of all AIP funds and over 50 percent of all PFC funds spent on noise reduction or mitigation have been used to acquire land and to soundproof buildings (see also, Residential Home Soundproofing section)

- LAX: $4 million

- ONT: $2.5 million

- Examples of AIP Funded Residential Home Soundproofing

- SNA: $2.3 million

- BUR: $1 million for 30 residences

- SFO: $1 million for 100 residences

- FAT: $1 million for 100 residences

- Examples of Federal, Local, or AIP Funded School Soundproofing

- JFK: $12.2 million for four schools

- LGA: $24.4 million for nine schools

- SYR: $3.38 million for a school

- ORD: $3 million for a school

- MDW: $3 million for a school

- SAN: $1.5 million for a school

- Examples of Litigation for Airport Noise

- DEN

- PBI

- EWR

- BUR

- MEM

- MSP

- ORD,

- BDL

### Reduction or Lifting of Airport Curfews

According to Boeing commercial noise data, 28 of the 121 studied airports, listed in Table 19, have noise-related curfews. By limiting the impact of noise on surrounding communities, LAAS-based procedures may permit airports to operate at times currently under curfew. Also, expansion of airport operating times by limiting or lifting of curfews can increase total daily capacity.

Table 19: Airports with Curfews within the 121 Studied Airports

| Airports with Noise-related Curfews (Curfew times in parentheses, when known) |
| --- |
| AUS (00:00 to 06:00) | HPN (00:00 to 06:30) | RIC (03:00 to 12:00) |
| BFI (22:00 to 07:00) | ILN | SAN (22:30 to 06:30) |
| BOS (23:00 to 07:00) | JFK (00:00 to 06:00) | SFO |
| BUR | LAS (20:00 to 08:00) | SJC (23:30 to 06:30) |
| DAL | LGB | SNA |
| DCA(22:00 to 07:00) | MDW (22:00 to 06:00) | STL (23:00 to 06:00) |
| DEN | MSP | SYR (02:00 to 07:00) |
| DVT (21:30 to 06:00) | ONT | VNY |
| FAI (3:00 to 06:00) | PBI (22:00 to 07:00) |  |
| HNL | PVD (0:00 to 07:00) |  |

## Reduced Impact on Environmentally Sensitive Areas

With the expansion of airports and communities surrounding airports, another growing concern is the impact of aviation-related activities on environmentally sensitive areas. Airlines and airframe manufacturers have worked together to significantly reduce the environmental impact produced by modern aircraft, but this remains a problem for some airports.  More precise navigation in the terminal area may offer an opportunity to greatly reduce the environmental impact of flights by restricting aircraft to defined three dimensional routes designed with environmentally sensitive areas in mind.

Through the flexibility offered by LAAS to construct complex, defined, highly repeatable flight paths that can be used during all weather conditions, environmentally sensitive areas may be protected during all weather conditions.  This section identifies the LAAS capabilities that can support environmental sensitive area efforts, and summarizes some of the current areas that may be potential beneficiaries.

Reduced impact on environmentally sensitive areas may be possible with RNAV capabilities through the use of GPS and/or WAAS.  In these cases, LAAS may show little to no benefit.

The FAA has a long tradition of designating wildlife and conservation areas as advisory noise-sensitive areas on navigational charts and other published materials. This practice, as articulated in Advisory Circular 91-36C ("Visual Flight Rules (VFR) Flight Near Noise-Sensitive Areas”), seeks to achieve a non-regulatory, cooperative approach to eliminating low overflights which would be harmful to wildlife in refuges and other environmentally-sensitive areas, including National Parks, Wilderness Areas, and their individual State Park or Conservation Area/Wildlife Refuge counterparts. It reflects the FAA’s announced policy of managing the airspace to protect environmental values on the surface.

### Methodology

- Identify LAAS capabilities that may offer control over the impact of aircraft operations on environmentally sensitive areas.

### Relevant LAAS Capabilities

The LAAS capabilities that may have a direct impact on environmentally sensitive areas are those that offer increased control over the flight path taken.  The ability to consistently provide defined, repeatable (laterally and vertically contained) flight tracks during all weather conditions allows for reduced impact on environmentally sensitive areas.

### Example Airports with Environmentally Sensitive Areas

The following examples provide a list of airports with environmentally sensitive areas.  These areas may be protected now, and into the future with airport expansion, through the use of defined, repeatable flight paths using all weather complex approach and departure procedures. See Figure 7 for an example of a defined, repeatable flight path.

Example airports with environmentally sensitive areas: BOS, CVG , DCA, SEA

## LAAS as a Complement to Homeland Security

Increased emphasis on aviation security requires precise navigation and surveillance capabilities.  The ability of LAAS to provide increased control over flight paths may be crucial to Homeland Security.  For example, in areas of heightened security, such as DCA in our nation’s capitol, LAAS coupled with other technologies, such as ADS-B, may enable Air Traffic to precisely anticipate an aircraft’s expected terminal area flight path, and more readily detect and react to any deviation from that flight path.

RNAV capabilities achieved through the use of GPS and/or WAAS, and other technologies, such as ADS-B, may also enable Air Traffic to precisely anticipate the expected terminal area flight path, and to more readily detect and react to any deviation from that flight path.  In these cases, LAAS may show little to no benefit.

### Methodology

- Identify airports within the 121 airports studied that have Aviation Defense Identification Zones (ADIZ) or temporary flight restrictions, as examples of airport and airspace locations where the ability to identify and detect deviations from expected flight paths may have been beneficial.

### Relevant LAAS Capabilities

The LAAS capabilities that may have a direct impact on Homeland Security are those that offer increased control over the flight path taken.  LAAS may be coupled with an enabled technology that provides aircraft position information to Air Traffic (e.g., ADS-B), for surveillance purposes.

### Example Airports with Aviation Defense Identification Zones (ADIZ) or Temporary Flight Restrictions (TFR)

Table 20 lists examples of airports in the 121 airports studied that have been subject to an ADIZ or TFR.

Table 20: Airports with ADIZ or TFR

| Airport | Comments |
| --- | --- |
| NY Area | Flight Restrictions for the 2004 Republican National Convention in New York City. |
| DCA | “National Capital Region (NCR) Aviation Defense Identification Zone (ADIZ) remains active with the added requirement that all VFR and IFR flights within the ADIZ file flight plans before takeoff and close flight plans upon landing or exiting the ADIZ”. |
| JFK, LGA, EWR | “An ADIZ for New York City has also been added restricting flight operations from the surface to flight level 180 in the area within the mode C veil (approximately 30 nm) surrounding JFK International (JFK), LaGuardia International (LGA), and Newark, New Jersey (EWR) International airports”. |
| MIA, EWR, JFK, LGA, DAY, DTW, MHT, BNA, CMH | Presidential movement TFRs Examples of presidential TFRs, that can be issued with little advance notice.. August 27: Miami, Florida August 29-30: Newark, New Jersey, and New York, New York August 30-September 1: New York, New York September 1-3: New York, New York Anticipated - August 28: Dayton, Ohio Anticipated - August 28: Lima, Ohio Anticipated - August 28: Toledo, Ohio Anticipated - August 28: Troy, Ohio Anticipated - August 29: Wheeling, West Virginia Anticipated - August 30: Detroit, Michigan Anticipated - August 30: Manchester, New Hampshire Anticipated - August 31: Alleman, Iowa Anticipated - August 31: Gettysburg, Pennsylvania Anticipated - August 31: Nashville, Tennessee Anticipated - September 1: Columbus, Ohio |
| ORD | Temporary Flight Restrictions (TFR) - March 22, 2003 “The FAA and TSA created a temporary flight restriction for the city of Chicago, focusing on the downtown skyline area”. |
| SLC | “Temporary Flight Restrictions (TFR) – Winter Olympics The FAA implemented a security plan that restricted general aviation operations within a 45-nm radius of Salt Lake City International Airport. The temporary flight restrictions area (TFR) extended from surface to 18,000 feet Mean Sea Level (MSL) for 19 days, beginning on February 6, 2001”. |
| ATL | Temporary Flight Restrictions (TFRs) Summer Olympics a radius of three nm around the Georgia Dome (below 3500 MSL) one nm around the Olympic Village (below 3500 MSL) |

## LAAS and JPALS Providing Civilian and Military Compatibility

The Department of Defense (DoD) currently operates a variety of precision approach systems, including ILS, MLS, and Precision Approach Radar (PAR).  No single system currently available meets all of the DoD’s precision approach needs (e.g., only one third of Navy aircraft, and one half of Army aircraft are ILS equipped).  In order to standardize on a single-system solution, the DoD is developing a Joint Precision Approach and Landing System (JPALS), a military-use differential GPS system designed to be interoperable with the civilian-use LAAS.  Interoperability of civil and military landing systems is the primary benefit.  A JPALS transmitter is designed to broadcast a signal meeting the requirements of civil LAAS avionics, and a JPALS receiver is designed to use the LAAS broadcast signal.

### Methodology

- Identify airports within the 121 studied airports that have a military presence that comprises greater than ten percent of total airport operations.

- Calculate the taxpayer dollars saved by avoiding redundant civilian and military systems.

  - It is assumed that a JPALS installation costs at least as much as a civil LGF, or $1.2M.

  - Tax Payer Savings equals ($1.2M/site) x (Number of studied airports that have a military presence that comprises greater than ten percent of total airport operations).

The twenty (20) airports shown in Table 21 are those within the 121 studied airports that have a military presence that comprises greater than ten percent of total airport operations.  In addition, the DoD has operations at many NAS airports, including over 95% of the 121 airports in this study.

Table 21: Studied Airports with Considerable (>10% of Total Operations) Military Operations

| Airport | % of Airport’s Traffic that are Military Operations | Airport | % of Airport’s Traffic that are Military Operations |
| --- | --- | --- | --- |
| ABQ | 15% | LIT | 19% |
| AFW | 18% | MDT | 13% |
| BGR | 34% | OKC | 37% |
| CHA | 14% | PIE | 12% |
| CHS | 38% | SHV | 13% |
| COS | 24% | SYR | 11% |
| DLH | 18% | TLH | 19% |
| HSV | 32% | TUL | 29% |
| JAX | 11% | TUS | 12% |
| LCK | 41% | TYS | 11% |

Note: Traffic estimates above may or may not be due to aircraft stationed at that airfield.

### Tax Payer Dollars Saved

Because of the interoperability of LAAS and JPALS, taxpayers may be able to forgo installing these two interoperable and compatible systems at one location.  At the 20 sites list above, this could potentially save taxpayers at least $24M.

## Expansion of Air Commerce to Smaller Communities

The expansion of air service to smaller communities can be important for economic development.  Allowing reliable, precision approach to all runways may increase economic development through increased air service and passenger utilization at smaller community airports.

The expansion of air commerce into smaller communities may have multiple beneficiaries.  Air Traffic and airlines may benefit from having increased alternative airports, and reduced congestion to major and larger community airports.  Airlines may benefit from expansion of their networks to new markets, potentially resulting in increased revenue passenger miles.  Residents of small communities may benefit from having access to increased air service, and small communities may benefit from the economic development that passengers and airlines bring.

Many of the benefits of expansion of air service may be achievable with RNAV capabilities through the use of GPS and/or WAAS, or achieved through ILS Category I/II/III precision approaches.  In these cases, LAAS may provide little or no benefit.  However, in some terrain challenged areas LAAS may be the best precision approach option.

Table 22 lists several example airports in small communities that may have terrain constraints. This list is not meant to be exhaustive, but to illustrate the types of airports in this category.

Table 22: Small Community Airports With ILS Terrain Challenges

| Airport Code | Airport Name | 2003 Scheduled Arrivals |
| --- | --- | --- |
| ASE | Aspen, CO | 4,162 |
| EGE | Eagle County, CO | 2,257 |
| SIT | Sitka, AK | 1,647 |
| JNU | Juneau, AK | 19,806 |
| SUN | Sun Valley, ID | 4,333 |

## Increased Reliability of Air Service

Studies have suggested that infrastructure changes that lead to increased quality of air service (e.g., reduced flight times, increased reliability) may lead to increased passenger load factors. By reducing delay and increasing all-weather reliability of air service, LAAS may offer this benefit.  Increased load factors will increase revenue in the Airport Improvement Program (AIP) through the Domestic Passenger Ticket Tax aviation component, and will also result in increased revenue to the airlines.  This analysis shows the 20 year benefits for a one percent (1%) increase in load factor on one percent (1%) of domestic and regional airline flights.

This quantification is for illustrative purposes only, and no claim is made that LAAS, or any other precision approach system will lead to these specific benefits.  Rather, this shows the benefits that may be obtained for every 1% increase in load factor on 1% of domestic major and regional operations, by improving the reliability of all-weather flight operations.

The Airport and Airway Trust Fund, which was established by the Airport and Airway Revenue Act of 1970, provides the revenues used to fund AIP projects.  The Trust Fund concept guarantees a stable funding source whereby users pay for the services they receive.  In 1997, Congress enacted new taxes to fund the Trust Fund as shown in Table 23.

Table 23: AIP Domestic Passenger Ticket Tax

| Aviation Component | Computation Formulae |
| --- | --- |
| Domestic Passenger Ticket Tax | 9% from Oct. 1, 1997 through Sept. 30, 1998 |
|  | 8% from Oct. 1, 1998 through Sept. 30, 1999 |
|  | 7.5% from Oct. 1, 1999 |

Methodology

- Estimate average ticket price per flight segment: $100.

- Estimate the average number of passengers per flight: 91 (average of B737)

- Assume 1% increase in load factor for 1% of airline operations due to improved reliability of air service.

- AIP Revenue is (avg. ticket price) x (domestic ticket tax) x (average number of passengers) x (% increase in load factor) x (% of airline operations that experience an increase in load factor by 1%) x (total U.S. airline operations at the 121 studied airports).

- Airline Revenue is (avg. ticket price) x (average number of passengers) x (% increase in load factor) x (% of airline operations that experience an increase in load factor by 1%) x (total U.S. airline operations at the 121 studied airports).

- Calculate the 20 year benefit using 2004 TAF projections.

- Calculate the 2004 present value using a 7% discount rate.

Results

As shown in Table 24, the estimated LAAS benefit assuming 0% WAAS equipage is $96M for each one percent (1%) increase in load factor on one percent (1%) of domestic major and regional carrier operations.

Table 24: Discounted 20 year LAAS Benefits for a 1% Increase in Load Factor on 1% of Domestic Major and Regional Airline Operations

|  | Increased AIP Revenue | Increased Airline Revenue | Total |
| --- | --- | --- | --- |
| LAAS Benefits (Assuming 0% WAAS equipage) | $6,701,079 | $89,347,725 | $96,048,805 |
| LAAS Benefits (Assuming 100% WAAS equipage) | $1,652,875 | $20,478,277 | $22,131,151 |

## LAAS Signal in the Vicinity of the 121 Studied Airports

Overview

The LAAS Concept of Operations (CONOPS), dated August 5, 2002, states the LAAS service coverage volume extends out to 23nm  radially from the LAAS Ground Facility VDB [Very High Frequency (VHF) Data Broadcast (VDB)] and with increasing altitude from the installed station (angle of 0.9 degrees, so that at 23 NM the minimum receivable altitude is 2200 ft).

IBM identified the aviation facilities (e.g., other airports, seaplane bases, gliderports, and heliports) within 23nm of each of the 121 studied airports from entries in the NFDC database.  Table 25 lists the results of this investigation, which identified: 1) 6,453 total aviation facilities within 23nm of all 121 airports, and 2) 428 total aviation facilities within 23nm of the 6 LRIP Airports.  This table shows the scope of potential beneficiaries of the LAAS signal if LAAS were installed at each of the 121 airports.

No claim of benefits is made for this potential capability, since the LAAS signal is not required or expected to meet minimum field strength requirements at low altitudes except at the airport where it is installed.  If a program decision were made to require LAAS services at these nearby airports, design and installation requirements would have to be updated to reflect this goal.  Alternatively, it may be feasible to exploit LAAS at these airports to some degree without any specific requirements on the design or installation (i.e., use LAAS where it is receivable).  It is not possible to estimate benefits in this scenario since the achieved coverage is not yet known.

Table 25.  Number of Aviation Facilities Within 23 nm of Each of the 121 Airports

The LAAS LRIP sites are shown in bold.

| Airport Code | # of Proximate Airports | Airport Code | # of Proximate Airports | Airport Code | # of Proximate Airports | Airport Code | # of Proximate Airports | Airport Code | # of Proximate Airports | Airport Code | # of Proximate Airports |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | 13 | CLE | 62 | FLL | 52 | LAS | 22 | ORD | 93 | SHV | 28 |
| ACK | 4 | CLT | 31 | FWA | 57 | LAX | 152 | ORF | 34 | SJC | 18 |
| AFW | 124 | CMH | 71 | FXE | 41 | LCK | 50 | PBI | 38 | SLC | 28 |
| ALB | 42 | COS | 23 | GEG | 32 | LGA | 104 | PDX | 99 | SMF | 37 |
| ANC | 24 | CVG | 39 | GRR | 34 | LGB | 161 | PHL | 148 | SNA | 81 |
| ATL | 75 | DAB | 23 | GSO | 30 | LIT | 35 | PHX | 78 | STL | 66 |
| AUS | 31 | DAL | 116 | GSP | 23 | MCI | 68 | PIE | 35 | SWF | 45 |
| AVL | 11 | DAY | 57 | HNL | 13 | MCO | 64 | PIT | 68 | SYR | 34 |
| BDL | 75 | DCA | 71 | HOU | 160 | MDT | 77 | PVD | 49 | TEB | 114 |
| BFI | 75 | DEN | 73 | HPN | 68 | MDW | 77 | RDU | 21 | TLH | 11 |
| BGR | 12 | DFW | 139 | HSV | 21 | MEM | 38 | RFD | 83 | TPA | 42 |
| BHM | 23 | DLH | 13 | IAD | 73 | MHT | 65 | RIC | 35 | TRI | 17 |
| BNA | 29 | DSM | 25 | IAH | 128 | MIA | 57 | RNO | 22 | TUL | 50 |
| BOI | 18 | DTW | 46 | ICT | 55 | MKE | 43 | ROC | 40 | TUS | 17 |
| BOS | 75 | DVT | 73 | ILN | 42 | MMU | 149 | RSW | 39 | TYS | 34 |
| BUF | 44 | ELP | 9 | IND | 94 | MSP | 72 | SAN | 20 | VNY | 137 |
| BUR | 138 | EUG | 27 | ISP | 32 | MSY | 40 | SAT | 59 |  |  |
| BWI | 70 | EWR | 141 | JAN | 25 | OAK | 32 | SDF | 31 |  |  |
| CAE | 21 | EYW | 6 | JAX | 28 | OKC | 57 | SEA | 85 |  |  |
| CHA | 18 | FAI | 13 | JFK | 86 | OMA | 35 | SFB | 56 |  |  |
| CHS | 10 | FAT | 26 | JNU | 6 | ONT | 53 | SFO | 26 |  |  |

There is a wide variety of facilities included in the list above.  To give a sample of these facilities, Appendix H details the 85 aviation facilities within 23nm of SEA.

# Appendices

## Appendix A:	Airports Included in This Study

Airports were selected for this study through an objective process that included the following criteria:

- High traffic airports associated with likely LAAS users:

  - Major passenger airlines (Airports with more than 20,000 operations over a three year period)

  - Regional passenger airlines (Regional Airline Association – Top 50 airports)

  - Cargo carriers

  - Corporate operators (National Business Aviation Association – Top 10 airports)

- LAAS Low Rate Initial Production (LRIP) sites

- FAA Operational Evolution Plan (OEP) airports

- Current Cat II/III ILS airports

- Qualifier Cat II/III ILS airports

Based on these criteria 121 airports throughout the NAS were selected for this study, as shown in Table A1 and the following map.

Table A1: 121 Airports Names and Locations Included in Study

| ABQ | ALBUQUERQUE INTL SUNPORT, NEW MEXICO | FAT | FRESNO YOSEMITE INTERNATIONAL, CALIFORNIA | OMA | EPPLEY AIRFIELD, NEBRASKA |
| --- | --- | --- | --- | --- | --- |
| ACK | NANTUCKET MEMORIAL, MASSACHUSETTS | FLL | FORT LAUDERDALE/HOLLYWOOD INTL, FLORIDA | ONT | ONTARIO INTL, CALIFORNIA |
| AFW | FORT WORTH ALLIANCE, TEXAS | FWA | FORT WAYNE INTERNATIONAL, INDIANA | ORD | CHICAGO O'HARE INTL, ILLINOIS |
| ALB | ALBANY INTL, NEW YORK | FXE | FORT LAUDERDALE EXECUTIVE, FLORIDA | ORF | NORFOLK INTL, VIRGINIA |
| ANC | TED STEVENS ANCHORAGE INTL, ALASKA | GEG | SPOKANE INTL, WASHINGTON | PBI | PALM BEACH INTL, FLORIDA |
| ATL | THE WILLIAM B HARTSFIELD ATLANTA INTL, GEORGIA | GRR | GERALD R. FORD INTERNATIONAL, MICHIGAN | PDX | PORTLAND INTL, OREGON |
| AUS | AUSTIN-BERGSTROM INTL, TEXAS | GSO | PIEDMONT TRIAD INTERNATIONAL, NORTH CAROLINA | PHL | PHILADELPHIA INTL, PENNSYLVANIA |
| AVL | ASHEVILLE REGIONAL, NORTH CAROLINA | GSP | GREENVILLE-SPARTANBURG INTL, SOUTH CAROLINA | PHX | PHOENIX SKY HARBOR INTL, ARIZONA |
| BDL | BRADLEY INTL, CONNECTICUT | HNL | HONOLULU INTL, HAWAII | PIE | ST PETERSBURG- INTL, FLORIDA |
| BFI | BOEING FIELD/KING COUNTY INTL, WASHINGTON | HOU | WILLIAM P HOBBY, TEXAS | PIT | PITTSBURGH INTL, PENNSYLVANIA |
| BGR | BANGOR INTL, MAINE | HPN | WESTCHESTER COUNTY, NEW YORK | PVD | T.F. GREEN STATE, RHODE ISLAND |
| BHM | BIRMINGHAM INTL, ALABAMA | HSV | HUNTSVILLE INTL-CARL T JONES FIELD, ALABAMA | RDU | RALEIGH-DURHAM INTL, NORTH CAROLINA |
| BNA | NASHVILLE INTL, TENNESSEE | IAD | WASHINGTON DULLES INTL, DIST. OF COLUMBIA (VA) | RFD | GREATER ROCKFORD, ILLINOIS |
| BOI | BOISE AIR TERMINAL/GOWEN FLD, IDAHO | IAH | GEORGE BUSH INTERCONTINENTAL ARPT/HOUSTON, TEXAS | RIC | RICHMOND INTL, VIRGINIA |
| BOS | GENERAL EDWARD LAWRENCE LOGAN INTL, MASSACHUSETTS | ICT | WICHITA MID-CONTINENT, KANSAS | RNO | RENO/TAHOE INTL, NEVADA |
| BUF | BUFFALO NIAGARA INTL, NEW YORK | ILN | AIRBORNE AIRPARK, OHIO | ROC | GREATER ROCHESTER INTL, NEW YORK |
| BUR | BURBANK-GLENDALE-PASADENA, CALIFORNIA | IND | INDIANAPOLIS INTL, INDIANA | RSW | SOUTHWEST FLORIDA INTL, FLORIDA |
| BWI | BALTIMORE-WASHINGTON INTL, MARYLAND | ISP | LONG ISLAND MAC ARTHUR, NEW YORK | SAN | SAN DIEGO INTL-, CALIFORNIA |
| CAE | COLUMBIA METROPOLITAN, SOUTH CAROLINA | JAN | JACKSON INTERNATIONAL, MISSISSIPPI | SAT | SAN ANTONIO INTL, TEXAS |
| CHA | LOVELL FIELD, TENNESSEE | JAX | JACKSONVILLE INTL, FLORIDA | SDF | LOUISVILLE INTL-, KENTUCKY |
| CHS | CHARLESTON AFB/INTL, SOUTH CAROLINA | JFK | JOHN F KENNEDY INTL, NEW YORK | SEA | SEATTLE-TACOMA INTL, WASHINGTON |
| CLE | CLEVELAND-HOPKINS INTL, OHIO | JNU | JUNEAU INTL, ALASKA | SFB | ORLANDO SANFORD, FLORIDA |
| CLT | CHARLOTTE/DOUGLAS INTL, NORTH CAROLINA | LAS | MC CARRAN INTL, NEVADA | SFO | SAN FRANCISCO INTL, CALIFORNIA |
| CMH | PORT COLUMBUS INTL, OHIO | LAX | LOS ANGELES INTL, CALIFORNIA | SHV | SHREVEPORT REGIONAL, LOUISIANA |
| COS | CITY OF COLORADO SPRINGS MUNI, COLORADO | LCK | RICKENBACKER INTERNATIONAL, OHIO | SJC | SAN JOSE INTL, CALIFORNIA |
| CVG | CINCINNATI/NORTHERN KENTUCKY INTL, KENTUCKY | LGA | LA GUARDIA, NEW YORK | SLC | SALT LAKE CITY INTL, UTAH |
| DAB | DAYTONA BEACH INTL, FLORIDA | LGB | LONG BEACH /DAUGHERTY FIELD/, CALIFORNIA | SMF | SACRAMENTO INTL, CALIFORNIA |
| DAL | DALLAS LOVE FIELD, TEXAS | LIT | ADAMS FIELD, ARKANSAS | SNA | JOHN WAYNE ORANGE COUNTY, CALIFORNIA |
| DAY | JAMES M COX DAYTON INTL, OHIO | MCI | KANSAS CITY INTL, MISSOURI | STL | LAMBERT-ST LOUIS INTL, MISSOURI |
| DCA | RONALD REAGAN WASHINGTON NATIONAL, DIST. OF COLUMBIA | MCO | ORLANDO INTL, FLORIDA | SWF | STEWART INT'L, NEW YORK |
| DEN | DENVER INTL, COLORADO | MDT | HARRISBURG INTERNATIONAL, PENNSYLVANIA | SYR | SYRACUSE HANCOCK INTL, NEW YORK |
| DFW | DALLAS/FORT WORTH INTERNATIONAL, TEXAS | MDW | CHICAGO MIDWAY, ILLINOIS | TEB | TETERBORO, NEW JERSEY |
| DLH | DULUTH INTL, MINNESOTA | MEM | MEMPHIS INTL, TENNESSEE | TLH | TALLAHASSEE REGIONAL, FLORIDA |
| DSM | DES MOINES INTL, IOWA | MHT | MANCHESTER, NEW HAMPSHIRE | TPA | TAMPA INTL, FLORIDA |
| DTW | DETROIT METROPOLITAN WAYNE COUNTY, MICHIGAN | MIA | MIAMI INTL, FLORIDA | TRI | TRI-CITIES RGNL TN/VA, TENNESSEE |
| DVT | PHOENIX DEER VALLEY, ARIZONA | MKE | GENERAL MITCHELL INTERNATIONAL, WISCONSIN | TUL | TULSA INTL, OKLAHOMA |
| ELP | EL PASO INTL, TEXAS | MMU | MORRISTOWN MUNI, NEW JERSEY | TUS | TUCSON INTL, ARIZONA |
| EUG | MAHLON SWEET FIELD, OREGON | MSP | MINNEAPOLIS-ST PAUL INTL/WOLD-CHAMBERLAIN/, MINNESOTA | TYS | MC GHEE TYSON, TENNESSEE |
| EWR | NEWARK INTL, NEW JERSEY | MSY | LOUIS ARMSTRONG NEW ORLEANS INTL, LOUISIANA | VNY | VAN NUYS, CALIFORNIA |
| EYW | KEY WEST INTL, FLORIDA | OAK | METROPOLITAN OAKLAND INTL, CALIFORNIA |  |  |
| FAI | FAIRBANKS INTL, ALASKA | OKC | WILL ROGERS WORLD, OKLAHOMA |  |  |

### Map of Airports Included in this Study

## Appendix B: 	Order of Installation of LAAS Ground Facilities

The order in which LAAS ground facilities are installed is an important factor in the estimation of LAAS benefits.  For this study, airport installations are assumed to take place at a pace of 24 per year, and in order of greatest to least benefit; that is, the first installations will be at airports with the highest benefit.  In general, each airport receives one LAAS installation. The exception is DEN, which due to its large area, was assumed to require two LAAS installations (see Appendix I, #16).  A rank ordered list of airports is constructed by calculating the full 20-year discounted benefit, assuming LAAS is installed at all airports at IOC (June 2009 for Cat I; June 2013 for Cat II/III).  A separate rank ordering is obtained depending on whether user equipage of WAAS is assumed to be 0% or 100%, since this assumption changes the benefits at many airports, and thus, potentially changes the order among airports.  The following tables show the assumed date of installation at each of the 121 airports studied (LAAS LRIP sites, which are the first to be installed with Cat I LAAS are highlighted in bold).  Table B1 gives this list in alphabetical order by airport, Table B2 shows the time order of LAAS installations for the 0% WAAS and 100% WAAS equipage scenarios.

Table B1: Order of Installation of LAAS Ground Facilities – Alphabetical Listing

| Airport | 0% WAAS |  | 100% WAAS |
| --- | --- | --- | --- |
|  | Cat I | Cat II/III |  | Cat I | Cat II/III |
| ABQ | Dec-10 | Jun-16 |  | Sep-10 | Jun-16 |
| ACK |  | Feb-14 |  |  | Feb-14 |
| AFW |  | Feb-18 |  |  | Feb-18 |
| ALB | Mar-10 | Jun-14 |  |  | Jun-14 |
| ANC | Feb-10 | Dec-14 |  | Oct-09 | Dec-14 |
| ATL | Oct-10 | Sep-13 |  | Dec-09 | Sep-13 |
| AUS |  | May-15 |  |  | May-15 |
| AVL |  | Nov-16 |  |  | Nov-16 |
| BDL | Jan-10 | Mar-15 |  |  | Mar-15 |
| BFI |  | Mar-17 |  |  | Mar-17 |
| BGR |  | Sep-17 |  |  | Sep-17 |
| BHM | Jan-10 | Nov-17 |  | Apr-10 | Nov-17 |
| BNA | Jan-11 | Jul-16 |  |  | Jul-16 |
| BOI |  | Nov-15 |  |  | Nov-15 |
| BOS |  | Nov-13 |  |  | Nov-13 |
| BUF | Sep-11 | Oct-14 |  | Jul-11 | Oct-14 |
| BUR | Sep-09 | Feb-17 |  |  | Feb-17 |
| BWI |  | Jul-14 |  |  | Jul-14 |
| CAE | Apr-11 | Sep-16 |  | Apr-11 | Sep-16 |
| CHA | Jul-12 | Dec-17 |  | Sep-11 | Dec-17 |
| CHS | Feb-11 | Jun-16 |  | May-10 | Jun-16 |
| CLE | Oct-09 | Oct-14 |  | Oct-09 | Oct-14 |
| CLT |  | Oct-13 |  |  | Oct-13 |
| CMH |  | Apr-15 |  |  | Apr-15 |
| COS | Nov-10 | Jul-14 |  | Oct-10 | Jul-14 |
| CVG | Mar-10 | Dec-13 |  | Sep-09 | Dec-13 |
| DAB |  | Jun-17 |  |  | Jun-17 |
| DAL |  | Jun-15 |  |  | Jun-15 |
| DAY | Dec-10 | May-16 |  | Jul-10 | May-16 |
| DCA | Sep-09 | Oct-15 |  | Aug-11 | Oct-15 |
| DEN |  | Aug-13 |  |  | Aug-13 |
| DFW | Nov-09 | Jun-13 |  | Sep-09 | Jun-13 |
| DLH | Jun-12 | Apr-17 |  | Oct-11 | Apr-17 |
| DSM |  | May-16 |  |  | May-16 |
| DTW | Nov-09 | Sep-13 |  | Feb-11 | Sep-13 |
| DVT | Aug-12 |  |  |  |  |
| ELP |  | Apr-18 |  |  | Apr-18 |
| EUG | May-11 | Jan-16 |  | Jun-10 | Jan-16 |
| EWR |  | Nov-13 |  |  | Nov-13 |
| EYW | Dec-11 | Apr-18 |  | May-11 | Apr-18 |
| FAI | Nov-11 | Jul-17 |  |  | Jul-17 |
| FAT |  | Nov-17 |  |  | Nov-17 |
| FLL | Jun-11 | Dec-15 |  | Jun-10 | Dec-15 |
| FWA | Jul-10 | Jun-17 |  |  | Jun-17 |
| FXE | Jul-12 | Jun-18 |  | Dec-11 | Jun-18 |
| GEG | Jun-10 | Apr-15 |  | Apr-10 | Apr-15 |
| GRR | Aug-11 | Mar-15 |  |  | Mar-15 |
| GSO |  | Aug-14 |  |  | Aug-14 |
| GSP |  | Dec-16 |  |  | Dec-16 |
| HNL | Apr-10 | Mar-18 |  | May-11 | Mar-18 |
| HOU | Sep-11 | Dec-13 |  | Apr-11 | Dec-13 |
| HPN | Dec-11 | Mar-14 |  | Jul-10 | Mar-14 |
| HSV |  | Mar-17 |  |  | Mar-17 |
| IAD |  | Feb-14 |  |  | Feb-14 |
| IAH | Jun-09 | Oct-13 |  | Jun-09 | Oct-13 |
| ICT | Feb-11 | Aug-16 |  | Dec-10 | Aug-16 |
| ILN |  | Sep-16 |  |  | Sep-16 |
| IND |  | Sep-15 |  |  | Sep-15 |
| ISP | Jul-11 | Jan-15 |  |  | Jan-15 |
| JAN |  | Oct-17 |  |  | Oct-17 |
| JAX |  | Mar-16 |  |  | Mar-16 |
| JFK | Oct-11 | Nov-14 |  | Oct-11 | Nov-14 |
| JNU | Jun-09 | Jul-17 |  | Jun-09 | Jul-17 |
| LAS | Jul-11 | May-18 |  | Jun-11 | May-18 |
| LAX |  | Mar-14 |  |  | Mar-14 |
| LCK |  | Feb-18 |  |  | Feb-18 |
| LGA | Dec-09 | Aug-13 |  |  | Aug-13 |
| LGB | Apr-10 | Oct-15 |  | Dec-09 | Oct-15 |
| LIT | Feb-12 | May-17 |  | Mar-11 | May-17 |
| MCI |  | Dec-14 |  |  | Dec-14 |
| MCO | Sep-10 | Jul-15 |  |  | Jul-15 |
| MDT |  | Apr-16 |  |  | Apr-16 |
| MDW | Apr-12 | Jul-13 |  | Jul-11 | Jul-13 |
| MEM | Jul-09 | Apr-14 |  | Jul-09 | Apr-14 |
| MHT | Aug-10 | Apr-14 |  | Mar-10 | Apr-14 |
| MIA | Jul-10 | Aug-15 |  | Mar-10 | Aug-15 |
| MKE | Dec-09 | Aug-14 |  | Nov-09 | Aug-14 |
| MMU | Jan-12 | Dec-17 |  | Jan-11 | Dec-17 |
| MSP |  | May-14 |  |  | May-14 |
| MSY | May-10 | Sep-15 |  | Feb-10 | Sep-15 |
| OAK | Feb-12 | Jul-16 |  |  | Jul-16 |
| OKC | Sep-10 | Feb-16 |  | Feb-10 | Feb-16 |
| OMA |  | Aug-16 |  |  | Aug-16 |
| ONT |  | Sep-17 |  |  | Sep-17 |
| ORD | Jul-09 | Jun-13 |  | Jul-09 | Jun-13 |
| ORF | Mar-12 | Sep-14 |  | Feb-11 | Sep-14 |
| PBI | Mar-11 | Dec-16 |  | Nov-10 | Dec-16 |
| PDX | May-12 | Jun-15 |  | Nov-11 | Jun-15 |
| PHL |  | May-14 |  |  | May-14 |
| PHX | Aug-09 | May-15 |  | Aug-09 | May-15 |
| PIE | Jan-12 | Aug-17 |  | Sep-11 | Aug-17 |
| PIT |  | Jan-14 |  |  | Jan-14 |
| PVD | Jan-11 | Nov-14 |  | Aug-10 | Nov-14 |
| RDU | Apr-12 | Jan-15 |  | Aug-11 | Jan-15 |
| RFD | Apr-11 | Oct-16 |  | Jan-11 | Oct-16 |
| RIC | May-10 | Jul-15 |  | Jan-10 | Jul-15 |
| RNO | Aug-10 | Apr-17 |  | May-10 | Apr-17 |
| ROC | Mar-11 | Nov-16 |  | Jan-10 | Nov-16 |
| RSW |  | Jun-14 |  |  | Jun-14 |
| SAN | Oct-09 | Feb-17 |  |  | Feb-17 |
| SAT |  | Feb-16 |  |  | Feb-16 |
| SDF |  | May-17 |  |  | May-17 |
| SEA | Aug-09 | Jan-14 |  | Aug-09 | Jan-14 |
| SFB | Aug-12 | Jan-18 |  | Nov-11 | Jan-18 |
| SFO |  | Jan-16 |  |  | Jan-16 |
| SHV | May-11 | Oct-17 |  | Dec-10 | Oct-17 |
| SJC | Feb-10 | Sep-14 |  | Nov-09 | Sep-14 |
| SLC | Oct-10 | Feb-15 |  | Aug-10 | Feb-15 |
| SMF |  | Aug-15 |  |  | Aug-15 |
| SNA | Mar-12 | Feb-15 |  | Dec-11 | Feb-15 |
| STL |  | Nov-15 |  |  | Nov-15 |
| SWF | Aug-11 | Mar-18 |  | Jun-11 | Mar-18 |
| SYR | Jun-11 | Jan-17 |  | Oct-10 | Jan-17 |
| TEB | Jun-10 | Apr-16 |  | Mar-11 | Apr-16 |
| TLH |  | Mar-16 |  |  | Mar-16 |
| TPA | Nov-10 | Dec-15 |  | Sep-10 | Dec-15 |
| TRI | May-12 | Jan-18 |  |  | Jan-18 |
| TUL | Oct-11 | Jan-17 |  | Nov-10 | Jan-17 |
| TUS | Jun-12 | May-18 |  |  | May-18 |
| TYS |  | Oct-16 |  |  | Oct-16 |
| VNY | Nov-11 | Aug-17 |  | Jan-12 | Aug-17 |

Table B2: Order of Installation of LAAS Ground Facilities – Date Ordered -  0% WAAS  and 100% WAAS Equipage Scenarios

| Airport | 0% WAAS |  | Airport | 100% WAAS |
| --- | --- | --- | --- | --- |
|  | Cat I | Cat II/III |  |  | Cat I | Cat II/III |
| IAH | Jun-09 | Oct-13 |  | IAH | Jun-09 | Oct-13 |
| JNU | Jun-09 | Jul-17 |  | JNU | Jun-09 | Jul-17 |
| ORD | Jul-09 | Jun-13 |  | ORD | Jul-09 | Jun-13 |
| MEM | Jul-09 | Apr-14 |  | MEM | Jul-09 | Apr-14 |
| SEA | Aug-09 | Jan-14 |  | SEA | Aug-09 | Jan-14 |
| PHX | Aug-09 | May-15 |  | PHX | Aug-09 | May-15 |
| DCA | Sep-09 | Oct-15 |  | DFW | Sep-09 | Jun-13 |
| BUR | Sep-09 | Feb-17 |  | CVG | Sep-09 | Dec-13 |
| CLE | Oct-09 | Oct-14 |  | CLE | Oct-09 | Oct-14 |
| SAN | Oct-09 | Feb-17 |  | ANC | Oct-09 | Dec-14 |
| DFW | Nov-09 | Jun-13 |  | MKE | Nov-09 | Aug-14 |
| DTW | Nov-09 | Sep-13 |  | SJC | Nov-09 | Sep-14 |
| LGA | Dec-09 | Aug-13 |  | ATL | Dec-09 | Sep-13 |
| MKE | Dec-09 | Aug-14 |  | LGB | Dec-09 | Oct-15 |
| BDL | Jan-10 | Mar-15 |  | RIC | Jan-10 | Jul-15 |
| BHM | Jan-10 | Nov-17 |  | ROC | Jan-10 | Nov-16 |
| SJC | Feb-10 | Sep-14 |  | MSY | Feb-10 | Sep-15 |
| ANC | Feb-10 | Dec-14 |  | OKC | Feb-10 | Feb-16 |
| CVG | Mar-10 | Dec-13 |  | MHT | Mar-10 | Apr-14 |
| ALB | Mar-10 | Jun-14 |  | MIA | Mar-10 | Aug-15 |
| LGB | Apr-10 | Oct-15 |  | GEG | Apr-10 | Apr-15 |
| HNL | Apr-10 | Mar-18 |  | BHM | Apr-10 | Nov-17 |
| RIC | May-10 | Jul-15 |  | CHS | May-10 | Jun-16 |
| MSY | May-10 | Sep-15 |  | RNO | May-10 | Apr-17 |
| GEG | Jun-10 | Apr-15 |  | FLL | Jun-10 | Dec-15 |
| TEB | Jun-10 | Apr-16 |  | EUG | Jun-10 | Jan-16 |
| MIA | Jul-10 | Aug-15 |  | HPN | Jul-10 | Mar-14 |
| FWA | Jul-10 | Jun-17 |  | DAY | Jul-10 | May-16 |
| MHT | Aug-10 | Apr-14 |  | PVD | Aug-10 | Nov-14 |
| RNO | Aug-10 | Apr-17 |  | SLC | Aug-10 | Feb-15 |
| MCO | Sep-10 | Jul-15 |  | TPA | Sep-10 | Dec-15 |
| OKC | Sep-10 | Feb-16 |  | ABQ | Sep-10 | Jun-16 |
| ATL | Oct-10 | Sep-13 |  | COS | Oct-10 | Jul-14 |
| SLC | Oct-10 | Feb-15 |  | SYR | Oct-10 | Jan-17 |
| COS | Nov-10 | Jul-14 |  | PBI | Nov-10 | Dec-16 |
| TPA | Nov-10 | Dec-15 |  | TUL | Nov-10 | Jan-17 |
| DAY | Dec-10 | May-16 |  | ICT | Dec-10 | Aug-16 |
| ABQ | Dec-10 | Jun-16 |  | SHV | Dec-10 | Oct-17 |
| PVD | Jan-11 | Nov-14 |  | RFD | Jan-11 | Oct-16 |
| BNA | Jan-11 | Jul-16 |  | MMU | Jan-11 | Dec-17 |
| CHS | Feb-11 | Jun-16 |  | DTW | Feb-11 | Sep-13 |
| ICT | Feb-11 | Aug-16 |  | ORF | Feb-11 | Sep-14 |
| ROC | Mar-11 | Nov-16 |  | TEB | Mar-11 | Apr-16 |
| PBI | Mar-11 | Dec-16 |  | LIT | Mar-11 | May-17 |
| CAE | Apr-11 | Sep-16 |  | HOU | Apr-11 | Dec-13 |
| RFD | Apr-11 | Oct-16 |  | CAE | Apr-11 | Sep-16 |
| EUG | May-11 | Jan-16 |  | HNL | May-11 | Mar-18 |
| SHV | May-11 | Oct-17 |  | EYW | May-11 | Apr-18 |
| FLL | Jun-11 | Dec-15 |  | SWF | Jun-11 | Mar-18 |
| SYR | Jun-11 | Jan-17 |  | LAS | Jun-11 | May-18 |
| ISP | Jul-11 | Jan-15 |  | MDW | Jul-11 | Jul-13 |
| LAS | Jul-11 | May-18 |  | BUF | Jul-11 | Oct-14 |
| GRR | Aug-11 | Mar-15 |  | RDU | Aug-11 | Jan-15 |
| SWF | Aug-11 | Mar-18 |  | DCA | Aug-11 | Oct-15 |
| HOU | Sep-11 | Dec-13 |  | PIE | Sep-11 | Aug-17 |
| BUF | Sep-11 | Oct-14 |  | CHA | Sep-11 | Dec-17 |
| JFK | Oct-11 | Nov-14 |  | JFK | Oct-11 | Nov-14 |
| TUL | Oct-11 | Jan-17 |  | DLH | Oct-11 | Apr-17 |
| FAI | Nov-11 | Jul-17 |  | PDX | Nov-11 | Jun-15 |
| VNY | Nov-11 | Aug-17 |  | SFB | Nov-11 | Jan-18 |
| HPN | Dec-11 | Mar-14 |  | SNA | Dec-11 | Feb-15 |
| EYW | Dec-11 | Apr-18 |  | FXE | Dec-11 | Jun-18 |
| PIE | Jan-12 | Aug-17 |  | VNY | Jan-12 | Aug-17 |
| MMU | Jan-12 | Dec-17 |  | DEN |  | Aug-13 |
| OAK | Feb-12 | Jul-16 |  | LGA |  | Aug-13 |
| LIT | Feb-12 | May-17 |  | CLT |  | Oct-13 |
| ORF | Mar-12 | Sep-14 |  | BOS |  | Nov-13 |
| SNA | Mar-12 | Feb-15 |  | EWR |  | Nov-13 |
| MDW | Apr-12 | Jul-13 |  | PIT |  | Jan-14 |
| RDU | Apr-12 | Jan-15 |  | ACK |  | Feb-14 |
| PDX | May-12 | Jun-15 |  | IAD |  | Feb-14 |
| TRI | May-12 | Jan-18 |  | LAX |  | Mar-14 |
| DLH | Jun-12 | Apr-17 |  | MSP |  | May-14 |
| TUS | Jun-12 | May-18 |  | PHL |  | May-14 |
| CHA | Jul-12 | Dec-17 |  | ALB |  | Jun-14 |
| FXE | Jul-12 | Jun-18 |  | RSW |  | Jun-14 |
| SFB | Aug-12 | Jan-18 |  | BWI |  | Jul-14 |
| DVT | Aug-12 |  |  | GSO |  | Aug-14 |
| DEN |  | Aug-13 |  | MCI |  | Dec-14 |
| CLT |  | Oct-13 |  | ISP |  | Jan-15 |
| BOS |  | Nov-13 |  | BDL |  | Mar-15 |
| EWR |  | Nov-13 |  | GRR |  | Mar-15 |
| PIT |  | Jan-14 |  | CMH |  | Apr-15 |
| ACK |  | Feb-14 |  | AUS |  | May-15 |
| IAD |  | Feb-14 |  | DAL |  | Jun-15 |
| LAX |  | Mar-14 |  | MCO |  | Jul-15 |
| MSP |  | May-14 |  | SMF |  | Aug-15 |
| PHL |  | May-14 |  | IND |  | Sep-15 |
| RSW |  | Jun-14 |  | BOI |  | Nov-15 |
| BWI |  | Jul-14 |  | STL |  | Nov-15 |
| GSO |  | Aug-14 |  | SFO |  | Jan-16 |
| MCI |  | Dec-14 |  | SAT |  | Feb-16 |
| CMH |  | Apr-15 |  | JAX |  | Mar-16 |
| AUS |  | May-15 |  | TLH |  | Mar-16 |
| DAL |  | Jun-15 |  | MDT |  | Apr-16 |
| SMF |  | Aug-15 |  | DSM |  | May-16 |
| IND |  | Sep-15 |  | BNA |  | Jul-16 |
| BOI |  | Nov-15 |  | OAK |  | Jul-16 |
| STL |  | Nov-15 |  | OMA |  | Aug-16 |
| SFO |  | Jan-16 |  | ILN |  | Sep-16 |
| SAT |  | Feb-16 |  | TYS |  | Oct-16 |
| JAX |  | Mar-16 |  | AVL |  | Nov-16 |
| TLH |  | Mar-16 |  | GSP |  | Dec-16 |
| MDT |  | Apr-16 |  | BUR |  | Feb-17 |
| DSM |  | May-16 |  | SAN |  | Feb-17 |
| OMA |  | Aug-16 |  | BFI |  | Mar-17 |
| ILN |  | Sep-16 |  | HSV |  | Mar-17 |
| TYS |  | Oct-16 |  | SDF |  | May-17 |
| AVL |  | Nov-16 |  | DAB |  | Jun-17 |
| GSP |  | Dec-16 |  | FWA |  | Jun-17 |
| BFI |  | Mar-17 |  | FAI |  | Jul-17 |
| HSV |  | Mar-17 |  | BGR |  | Sep-17 |
| SDF |  | May-17 |  | ONT |  | Sep-17 |
| DAB |  | Jun-17 |  | JAN |  | Oct-17 |
| BGR |  | Sep-17 |  | FAT |  | Nov-17 |
| ONT |  | Sep-17 |  | TRI |  | Jan-18 |
| JAN |  | Oct-17 |  | AFW |  | Feb-18 |
| FAT |  | Nov-17 |  | LCK |  | Feb-18 |
| AFW |  | Feb-18 |  | ELP |  | Apr-18 |
| LCK |  | Feb-18 |  | TUS |  | May-18 |
| ELP |  | Apr-18 |  | DVT |  |  |

## Appendix C: 	Derivation of Disruption Costs

Disruptions occur when there is an interruption to a planned or optimum flight schedule, and are categorized as delays, cancellations, and diversions. These disruptions have costs for both aircraft operators (Direct Operating Cost; DOC) and passengers (Passenger Time Savings; PTS).  Both DOC and PTS costs are assessed and reported by user type: Major passenger airlines, Regional airlines, Cargo carriers, Corporate jet operators, and General Aviation (GA).  The disruptions costs described in this section were used to calculate the LAAS benefits from straight-in and complex approaches.

### Direct Operating Costs

A weighted average delay cost was computed for direct operating cost of Major, Regional, Cargo, Corporate, and other GA assuming two-thirds of delays are ground delays and one-third occur in the air.  FAA APO data sources were used to obtain the recommended values.  For example, APO states that the ground delay for a Major carrier is $30.70 per minute and that the airborne cost is $43.85 per minute (see Table D3 in Appendix D). Taking 2/3*($30.70) + 1/3*($43.85) gives an average delay cost of $35.08 per minute for the Major carriers. Corporate jet DOC costs were provided by the FAA’s Office of Investment Analysis and Operations Research (ASD) including cost of crew, fuel and maintenance.

Cancellation costs were calculated assuming a typical mid size aircraft for Majors (i.e., MD80) and for Regional carriers (i.e., F100).  Based on inputs from airline representatives, it was assumed that Cargo operators do not cancel flights, so no cost was needed for this user group.  It was also assumed that since general aviation flights are not scheduled, corporate jet operators and other GA operators do not incur cancellations.

Diversion costs were derived from the Issue Paper analyzing “Schedule Disruptions” from the FAA’s Office of Aviation Policy and Plans (APO).  The estimated average hourly costs of the aircraft for diverted flights were obtained for Majors and Regional carriers.  It was further assumed that an average diversion time is approximately two hours, and the per hour costs were multiplied to obtain the total diversion cost per incident.

The average unit costs of disruptions used for DOC values are summarized in Table C1.

Table C1: Average DOC Delay, Cancellation, Diversion Costs (2004 dollars)

| Type of Disruption | Majors | Regional | Cargo | Corporate (NBAA) | General Aviation |
| --- | --- | --- | --- | --- | --- |
| Delay (per minute)* | $35.08 | $21.43 | $69.95 | $20.80 | $6.97 |
| Cancellation (per incident) | $6,820 | $2,132 | $0 | $0 | $0 |
| Diversion (per incident)** | $8,047 | $4,412 | $9,845 | $4,231 | $2,202 |

* Weighted Average direct operating cost

**Assume average duration of a diversion is 2 hours

### Passenger Time Savings

To monetize passenger benefits, the following PTS economic values were used, listed in Table C2 by user type.

Table C2: Breakdown of PTS (dollars/hr)

The Air Carrier’s All Purposes recommended values in Table C2 were used for Major and Regional users. General Aviation Business category was used for all corporate jet travelers.  General Aviation All Purposes was applied to all GA operations.

Aircraft capacity and utilization factors identified in Table C3 were applied to Passenger Time Savings to obtain total PTS per flight.

Table C3: Aircraft Capacity and Utilization Factors

| User Type | Assumed Aircraft Seating Capacity | Passenger Load Factor |
| --- | --- | --- |
| Major Carrier | 157 | 72% |
| Regional | 100 | 62% |
| Corporate | 10 | 50% |
| General Aviation | 6 | 60% |

### Results Summary:

A weighted average cost of a disruption was calculated using the observed occurrence of the three categories of disruption types.  Observed disruptions for major and regional airlines were analyzed based on scheduled arrivals from Airline Service Quality Performance (ASQP) database.  The proportion of each disruption type was then used to determine cargo, corporate, and GA disruptions.

An average duration of delay, used to compute the weighted average DOC and PTS, was determined based on ASQP gate arrival delay, with NCDC weather data used to isolate those delays occurring in Cat I/II/III conditions.  Delays greater than 15 minutes were extracted to calculate the point estimate.  Average delay during visual conditions was subtracted from these Cat I/II/III delays to obtain an average weather-related delay that is normalized for the amount of delay inherent in the NAS during operations in visual conditions. This resulted in an average weather-related delay of 45 minutes for Majors and Cargo carriers, and 37 minutes for Regional, Corporate, and GA.  Furthermore, since ASQP gate arrival delay includes the ripple effect, the average durations were divided by the ripple effect factor of 1.8.  This results in average delays of 25 and 21 minutes for Majors and Regional respectively.

Table C4 shows the average length of delay values used to compute weighted average disruption costs. See Appendix D for a detailed discussion of Sensitivity Analysis for Average Duration of Delay and Table D5 for the Delay Ranges used.

Table C4: Average Duration of Delay During Cat I/II/III Conditions

| User Type | Mean Delay |
| --- | --- |
| Major Carrier | 25 |
| Regional | 21 |
| Cargo | 25 |
| Corporate | 21 |
| General Aviation | 21 |

Table C5 provides the final weighted average disruption DOC and PTS costs by user type. Costs were computed using FAA-APO recommended values.

Table C5: Weighted Average Disruption Costs Per Incident by Carrier

| User Type | Direct Operating Cost | Passenger Time Savings | Total Cost |
| --- | --- | --- | --- |
| Major Carrier | $1,983 | $2,545 | $4,528 |
| Regional | $805 | $1,330 | $2,135 |
| Cargo | $1,903 | $0 | $1,903 |
| Corporate | $502 | $89 | $591 |
| General Aviation | $182 | $53 | $235 |

The impact of using an average disruption cost rather than a separate cost for each of the 121 airports was investigated.  While there are differences in disruption cost among airports, the net impact to the total benefits calculation was estimated to be less than 1%, which did not justify the additional complexity required to introduce airport-specific cost calculations.

### Data Sources:

- The DOT’s ASQP database was used for scheduled arrivals and disruption data from January 1998 to July 2003.  Outliers, such as the time period after September 11 and time periods associated with airline strikes were removed from the data.

- GRA Incorporated, Aviation Specialist Group Inc., Database Products, "Economic Values for FAA Investment and Regulatory Decisions, A Guide", Prepared for FAA Office of Aviation Policy and Plans, Final Report – May 28, 2004. [http://apo.faa.gov/arcc/Research.htm]

- Inflation Factors Source: Dept. of Commerce, Bureau of Economic Analysis, GDP Price Indexes. OMB's GDP Price Index Guidelines were applied for projection to 2004 dollars.

## Appendix D: 	Sensitivity Analyses

There is considerable uncertainty surrounding the proper values of several input parameters used in this benefits estimate.  A sensitivity analysis was conducted to determine the impact of this uncertainty on the estimated benefits.  This report on the LAAS efficiency benefits includes sensitivity analyses on five parameters:

- the cost of a disruption,

- the rate at which LAAS avionics equipage occurs,

- the minimum avionics equipage level required for benefit accrual,

- the downstream effect factor, and

- the average duration of delay.

These parameters were selected due to both the uncertainty of their values, and their central importance in building the benefits estimates.  Based on research of historical precedents, published estimates, and interviews with airline and other industry representatives, there is a wide range of opinion regarding the correct value to assign to the cost of a flight disruption, the likely pace at which users will install new technology avionics, the fraction of users that must be equipped before concerns about mixed-equipage operations are overcome, the correct downstream effect factor and the average duration of delay.  From this research, a range of expected values was developed for each of these parameters, including a central, or most likely value, as well as upper and lower bounds. In each case, the central value was first developed from research, and then validated with airline representatives, with the upper and lower bounds also emerging from these industry discussions.

The risk modeling approach selected for this analysis varies the parameter values between these upper and lower bounds in order to explore the extent to which the uncertainty in the parameter values may affect the benefits.  This risk analysis was conducted using @RISK, a commercial software tool, which employs Monte Carlo simulation to explore a large number of possible values of the uncertain parameters.

The sensitivity analysis was conducted in four steps. The first analysis varied parameter values of both direct operating costs and passenger time savings for the five user groups (major airlines, regional airlines, cargo carriers, corporate jets, and general aviation). A triangular distribution was applied, representing low, most likely and high values of these costs.  Table D1 shows the cost value ranges applied for the Straight-in and Complex Approaches analyses:

Table D1: Direct Operating Costs Ranges - Disruptions

| User Type | Low Estimate | Most Likely Estimate | High Estimate |
| --- | --- | --- | --- |
| Major Carrier | $782 | $1,983 | $4,269 |
| Regional | $700 | $805 | $1,035 |
| Cargo | $937 | $1,903 | $3,400 |
| Corporate | $297 | $502 | $767 |
| General Aviation | $145 | $182 | $237 |

Table D2 shows the cost value ranges applied to determine the Passenger Time Savings.

Table D2: Passenger Time Savings Costs Ranges - Disruptions

| User Type | Low Estimate | Most Likely Estimate | High Estimate |
| --- | --- | --- | --- |
| Major Carrier | $1,547 | $2,545 | $4,374 |
| Regional | $625 | $1,330 | $2,569 |
| Cargo | $0 | $0 | $0 |
| Corporate | $17 | $89 | $234 |
| General Aviation | $26 | $53 | $98 |

Table D3 shows the cost value ranges applied for the Take-off Guidance, ILS Critical Area, and Closely Spaced Simultaneous Independent Parallel Approach analyses.

Table D3: Ground and Airborne Delay Direct Operating Cost Ranges (Per Minute)

| User Type | Low Estimate | Most Likely Estimate | High Estimate |
| --- | --- | --- | --- |
|  | Ground / Airborne | Ground / Airborne | Ground / Airborne |
| Major Carrier | $27.63 / $39.47 | $30.70 / $43.85 | $33.77 / $48.24 |
| Regional | $16.88 / $24.11 | $18.75 / $26.79 | $20.63 / $29.47 |
| Cargo | $55.09 / $78.70 | $61.21 / $87.44 | $67.33 / $96.18 |
| Corporate | $14.04 / $28.08 | $15.60 / $31.20 | $17.16 / $34.32 |
| General Aviation | $5.49 / $7.84 | $6.10 / $8.71 | $6.71 / $9.58 |

Table D4 shows the cost value ranges applied for ground and airborne delay (per minute) PTS.

Table D4: Ground and Airborne Delay (Per Minute) Cost Ranges

| User Type | Low Estimate | Most Likely Estimate | High Estimate |
| --- | --- | --- | --- |
| Major Carrier | 41.33 | 53.88 | 72.54 |
| Regional | 13.88 | 29.55 | 57.08 |
| Cargo | - | - | - |
| Corporate | 0.74 | 3.75 | 9.89 |
| General Aviation | 1.08 | 2.33 | 4.13 |

In the second analysis, low, most likely, and high values of the time to equip and the minimum required equipage (or “critical mass”) was applied. These values are consistent with recommendations received through interviews with airline and air traffic control representatives:

- High: 5 years to equip with 0% critical mass,

- Most Likely: 6 years for fleet to equip with 80% critical mass and

- Low: 8 years equipage rate with 100% critical mass, respectively.

For the third analysis, a downstream effect range with low, most likely, and high was applied to the overall analysis and the takeoff guidance analysis.  Table D5 shows the downstream effect factors that were used and the bounds placed to conduct the sensitivity analysis.  These factors were received from SME inputs and additional research.  A more detailed discussion of the downstream effect factors can be found in Appendix N.

Table D5: Downstream Effect Ranges

| User Type | Low Estimate | Most Likely Estimate | High Estimate |
| --- | --- | --- | --- |
| All Analysis (except Takeoff Guidance) | 1.0 | 1.8 | 2.6 |
| Takeoff Guidance Analysis | 1.0 | 3.7 | 7.0 |

Finally, the fourth step varied the average duration of delay.  Weather delays greater than 0, 15, and 30 minutes were extracted for low, most likely and high values.  For Majors and Cargo operators, delays greater then 0 resulted in an average of 24 minutes, greater then 15 resulted in 45 minutes and above 30 resulted in an average of 73 minutes.  For remaining regional, corporate and general aviation aircraft and average of 37 minutes was used.  Furthermore, to exclude the ripple effect, these values were divided by the 1.8 factor.  Table D6 shows the average duration of delay used for the low, most likely and high ranges.

Table D6: Average Duration of Delay Ranges

| User Type | Low Estimate | Most Likely Estimate | High Estimate |
| --- | --- | --- | --- |
| Majors | 13 | 25 | 41 |
| Regional | 21 | 21 | 21 |
| Cargo | 13 | 25 | 41 |
| Corporate | 21 | 21 | 21 |
| General Aviation | 21 | 21 | 21 |

Conducting the sensitivity analysis using all these bounds produces risk-adjusted benefits for both direct operating cost and passenger time savings, for the two WAAS user equipage scenarios.  Figures D1 through D4 show the range of estimated LAAS benefits, highlighting the 5th and 95th percentiles.  Figures D1 and D2 show these results for direct operating costs and the 0% and 100% WAAS user equipage scenarios, respectively.  Figures D3 and D4 show these results for passenger time savings and the 0% and 100% WAAS user equipage scenarios, respectively.

Another output of the sensitivity analysis is an estimate of the relative influence that the uncertain parameters have on the benefits.  In both the 0% and 100% WAAS equipage scenarios for DOC, disruption cost is the most influential parameter followed closely by downstream effect.

Figure D1: Sensitivity Analysis: LAAS Direct Operating Cost Benefits - 0% WAAS scenario

Figure D2: Sensitivity Analysis: LAAS Direct Operating Cost Benefits - 100% WAAS scenario

Figure D3: Sensitivity Analysis: LAAS Passenger Time Savings - 0% WAAS scenario

Figure D4: Sensitivity Analysis: LAAS Passenger Time Savings - 100% WAAS

## Appendix E:	Derivation of the Single Airport Delay Model

The Single Airport Delay Model is a deterministic model that can be used to estimate delays at a single airport when demand exceeds capacity.  Since the model is deterministic, it does not take into account all of the delays that may occur due to the randomness of operations at a capacity constrained resource.  Nevertheless, it offers a very reasonable approximation to those delays.  This model is used in the Takeoff Guidance, ILS Critical Area, and Parallel Approach benefit sections.

### Basic Methodology and Illustrative Example

The model is based on a methodology described on pp. 339-343 of Robert Horonjeff’s and Francis McKelvey’s “Planning and Design of Airports” (4th edition, 1994).  The idea behind the model is fairly straightforward.  Any demand that cannot be satisfied by the available capacity during a particular period rolls over into the next period and contributes to delay.  If the capacity during that period is sufficient to handle the rollover demand plus the new demand arriving in that period, there is no additional delay.  However, if the demand exceeds the capacity, a rollover into the next period occurs once again and the delay accumulates.  The spreadsheet model calculates the average delay and a number of other metrics that summarize the performance of the airport.

A simple example can help illustrate how the model calculates delay.  Figure E1 illustrates the overall problem.  A given airport has insufficient capacity to handle the demand.  This demand can be in the form of arrivals, departures, or both, and the capacity can be for a single runway or multiple runways at the airport.  The unit of time is a quarter hour, but can just as well be any other value.  Note in this example that in the second quarter hour, the demand of 5 flights exceeds the capacity of 4 flights per 15 minute period.

Figure E1.  Illustrative Example of Demand and Capacity versus Time at an Airport

Figure E2 shows another way of representing this same data.  In this graph, the demand and capacity are depicted as cumulative functions over the specified time period.  Note that the cumulative capacity curve begins at the point in time when the demand rate starts to exceed the service rate or capacity (end of the first time period).  For any point in time after that on the horizontal axis (until the two curves intersect once again), the vertical distance between the two curves represents the total queue at that point in time.  Similarly, for any flight on the vertical axis, the horizontal distance between the two curves corresponds to the total delay experienced by that flight.  The area between the two curves is the total delay for all the flights in this five quarter hour period.

Figure E2.  Cumulative Demand and Capacity Versus Time

In order to simplify Figure E2, the difference between the cumulative demand and cumulative capacity is computed and the result is plotted as a function of time over the period of interest when the demand exceeds the capacity.  This effectively transforms Figure E2 into another graph (see Figure E3) with the y-value representing the total queue at any point in time.  Note that in addition to obtaining the queue length, a number of other performance measurements can also be derived from this graph.  For example, the maximum queue length can be easily seen to be 3.

Figure E3.  Difference Between Cumulative Demand and Cumulative Capacity as a Function of Time

Service time is the reciprocal of the capacity. For this particular example, the capacity is 16 aircraft/60 minutes, which gives a service time of 3.75 minutes per aircraft.  Therefore the value for the longest delayed aircraft can be obtained by multiplying the maximum queue length by 3.75 minutes, thus obtaining 3 x 3.75 minutes = 11.25 minutes.  The delay for all aircraft during any 15 minute period can be derived by calculating the area of the curve for that 15 minute period.  This amounts to calculating the area of one of the triangles or trapezoids labeled A, B, C, or D in Figure E3.  For example, the delay during the first 15 minute period is simply the area of triangle A -  ½ x base x height or ½ x 15 minutes x 1 = 7.5 minutes. Note that the calculation of the area of D is a little more complex since the function does not intersect the x-axis at a convenient break point (multiple of the quarter hour time interval).  Therefore, it is necessary to determine the exact point of intersection before the calculation can be performed.

Once the areas under the curve are determined for each quarter hour period, the total delay for all aircraft during the entire period can be obtained by summing the areas of all these triangles and trapezoids.  In this example, this area turns out to be 85 minutes.  The average delay per aircraft is then simply the total delay divided by the number of aircraft or 85 minutes/16 aircraft = 5.3 minutes/aircraft.

### Inputs and Outputs in the Model

### Model Input: Estimated Total Traffic

The total traffic demand at an airport, a key input to the Single Airport Delay Model, is estimated for each fifteen minute time period for a typical day by using the scheduled volume and factoring in an estimate of unscheduled traffic. The total traffic is built up from three elements; 1) scheduled, 2) unscheduled IFR, and 3) VFR traffic.  To address these three elements, three data sources from FAA-APO were used for this analysis: Flight Schedule Data System (FSDS), Enhanced Traffic Management System Counts (ETMSC), and Operations Network (OPSNET).

Scheduled volume was obtained from the FSDS database, using April 30, 2003 as a representative traffic volume day.  This date was selected because the arrival count for that date had the median volume, nationwide, of the 2003 calendar year. Scheduled traffic is allotted to 15 minute periods throughout the day.  To add unscheduled volume, ETMSC data, which include both scheduled and unscheduled IFR traffic, was obtained.  Four Wednesdays within the same month were selected, April 9, 16, 23 and 30, 2003 to obtain a representative sampling of the variability of this unscheduled traffic. An average ETMSC count of arrivals and departures for these four days was calculated and the number of flights above and beyond the scheduled traffic was then added to the original FSDS-based daily volume.  These flights were added randomly to 15 minute periods over the 24 hours of the day. VFR traffic was added through a similar process. Flight counts were obtained from OPSNET, which includes both IFR and VFR flights. OPSNET flight counts above and beyond the average ETMSC traffic represent an estimate of VFR traffic, and were added to the scheduled and unscheduled traffic. Since these VFR flights typically occur during daylight hours, this volume was added randomly between 6am and 10pm to complete the total traffic estimate.

#### Example:

To illustrate the method of building the total traffic, the following chart shows simulated numbers of arrivals reported by each database, for an imaginary example airport, ABC, on April 30th, 2003.

| Airport | FSDS Arrivals | ETMSC Arrivals | OPSNET Arrivals |
| --- | --- | --- | --- |
| ABC | 200 | 224 | 240 |

The 200 scheduled FSDS arrivals are allotted to their proper quarter-hour periods.  ETMSC reports 24 additional arrivals beyond those in FSDS.  A random number generator was used to assign these 24 flights to quarter-hour time slots, adding these to the FSDS arrivals already in those quarter-hours. NOTE: The random number generator allows for replacement, so any quarter-hour throughout the day can have any number of these 24 flights added to it.

The random assignment process is repeated for the additional 16 OPSNET arrivals above and beyond those recorded in the ETMSC database. These sixteen flights will be added at random to the new volume calculated from the FSDS + ETMSC data.  The end result is an estimate of the total traffic encountered at an airport, and it is used as an input to IBM’s Single Airport Delay Model to simulate the actual flights that arrive and depart at each airport on that day.

Table E1  below illustrates how these arrivals might be assigned to quarter-hour periods to build a total number of arrivals for each period.  Only part of a complete 24 hour day is shown for this example.

Table E1.  Illustrative Example of Building Total Traffic

| Time Period | FSDS Arrivals | ETMSC Arrivals | OPSNET Arrivals | Total Arrivals |
| --- | --- | --- | --- | --- |
| . |  |  |  |  |
| . |  |  |  |  |
| . |  |  |  |  |
| 8:00 | 12 |  |  | 12 |
| 8:15 | 11 | 1 |  | 12 |
| 8:30 | 13 |  | 4 | 17 |
| 8:45 | 9 |  |  | 9 |
| 9:00 | 6 | 2 | 1 | 9 |
| 9:15 | 4 |  |  | 4 |
| 9:30 | 3 | 4 |  | 7 |
| 9:45 | 5 | 1 |  | 6 |
| 10:00 | 3 |  | 1 | 4 |
| 10:15 | 6 |  |  | 6 |
| 10:30 | 10 |  |  | 10 |
| 10:45 | 11 |  |  | 11 |
| 11:00 | 12 | 2 |  | 14 |
| 11:15 | 5 |  |  | 5 |
| 11:30 | 6 |  |  | 6 |
| 11:45 | 3 |  |  | 3 |
| 12:00 | 0 | 3 | 1 | 4 |
| 12:15 | 8 |  |  | 8 |
| 12:30 | 7 |  |  | 7 |
| 12:45 | 4 | 1 |  | 5 |
| 13:00 | 0 |  |  | 0 |
| . |  |  |  |  |
| . |  |  |  |  |
| . |  |  |  |  |

Continuing the example from Figure E3, Table E2 shows the values derived by the model for this illustrative example, including all of the critical system performance parameters.

Table E2.  Single Airport Delay Model Inputs and Results for Illustrative Example

| Quarter Hour | Demand (D) | Capacity (C) | D - C | # of Aircraft in Queue | Delays/Quarter Hour | Dem>Cap? | A/C in Queue? |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0:15 | 1 | 4 | -3 | 0 |  | 0 | 0 |
| 0:30 | 5 | 4 | 1 | 1 | 7.5 | 1 | 1 |
| 0:45 | 6 | 4 | 2 | 3 | 30.0 | 1 | 1 |
| 1:00 | 3 | 4 | -1 | 2 | 37.5 | 0 | 1 |
| 1:15 | 1 | 4 | -3 | 0 | 10.0 | 0 | 0 |
|  | 16 |  |  |  |  |  |  |
| Total delay = | 85.0 | minutes | or | 1.4 | hours |
| Average delay per aircraft = | 5.3 | min/aircraft |  |  |  |
| Largest number of aircraft delayed = | 3 | aircraft |  |  |  |
| Delay time for longest-delayed aircraft = | 11.3 | minutes |  |  |  |
| # of quarter hours when demand>cap = | 2 |  | or | 40% | of the time |
| # of quarter hours when ac in queue = | 3 |  | or | 60% | of the time |

The inputs to the model are the demand and the capacity.  Demand at each airport was estimated as described above, using the scheduled volume and factoring in an estimate of unscheduled traffic.  Airport capacity data was provided by FAA ASD-430.

The model simply calculates the difference between the demand and capacity during each period.  The “#of Aircraft in Queue” column contains the queue lengths (shown as y-axis values (Aircraft In Queue) in Figure E3).  They are obtained by calculating the difference between the overall demand (flights left over from the previous period plus those arriving in this period) and the capacity.  Negative values are set equal to zero since a negative queue length is not allowed.

The “Delays/Quarter Hour” are obtained by calculating the areas of the triangles and trapezoids as described earlier (in reference to Figure E3).   The last two columns are simply set to 1 when the fourth and fifth columns, respectively, are greater than 0.

### Model Outputs

The highlighted metrics at the bottom of the table summarize the results of the computations.  The methods for deriving the first four values were described previously.  The last two metrics are obtained by taking the sum of the last two columns and dividing by the total number of quarter hour periods to obtain the “# of quarter hours when demand exceeds capacity” and the “# of quarter hours when aircraft are in queue”, respectively.

### Summary

In summary, it is important to note that the Single Airport Delay Model is extremely simple to use and can be easily adapted to determine delays associated with any demand and capacity imbalance.  It is not restricted to aircraft and airports, but in fact can be used for a wide variety of applications.  In particular, it has already proven to be useful in determining delays that may occur from the introduction of new security screening equipment and procedures at airline cargo facilities.

## Appendix F:	Navigation Capabilities Baseline

LAAS benefits are estimated relative to a baseline of existing and planned systems.  This baseline was defined in the Navigation Capabilities Baseline delivered November 2003.  The following three tables, excerpted from the earlier deliverable, contain the key elements of the baseline:

F1. NAS Baseline 	– existing and planned ground and space-based infrastructure

F2. System Capabilities 	– capabilities associated with existing and planned systems

F3.User Baseline		– estimates of avionics equipage levels for the relevant systems

Table F1 lists the NAS Capabilities Baseline at each runway associated with the 121 studied airports.  Any system available before or during year 2005 is given a value of 2005.

### Table F1: NAS Baseline

Table F2: System Capabilities

Table F3: User Baseline

## Appendix G:	Potential LAAS Sites Outside of the 121 Airports

The following airports, listed in alphabetical order, have been identified by airline representatives as potential LAAS candidate airports outside the 121 studied airports.

Table G1.  Potential LAAS Sites Outside of the 121 Airports

| Airport Code | Location | 2003 Scheduled Arrivals |
| --- | --- | --- |
| ASE | Aspen, CO | 4,162 |  |
| EAT | Wenatchee, WA | 2,334 |  |
| EGE | Eagle County, CO | 2,257 |  |
| GUC | Gunnison County, CO | 1,387 |  |
| JAC | Jackson Hole, WY | 4,979 |  |
| PUW | Pullman, WA | 1,744 |  |
| SIT | Sitka, AK | 1,647 |  |
| SUN | Sun Valley, ID | 4,333 |  |
| YAK | Yakutat, AK | 1,196 |  |

### Limitations

- Lack of operational data precludes analyzing these airports at the same level of detail as was performed for the IBM 121 Airports.

- Analysis of airports outside of the original list of 121 is currently out of scope for this study.

## Appendix H:	LAAS Signal in the Vicinity of the 121 Studied Airports - Example

Table H1 details the 85 aviation facilities within 23nm of Seattle-Tacoma Airport (SEA).

Table H1.  Aviation Facilities Within 23 nm of SEA

| Airport Code | Airport Name | City | State |
| --- | --- | --- | --- |
| 02WA | CAWLEYS SOUTH PRAIRIE | SOUTH PRAIRIE | WA |
| 08WA | MANCHESTER LABORATORY | MANCHESTER | WA |
| 0S8 | PORT ORCHARD | PORT ORCHARD | WA |
| 0W0 | SEATTLE SEAPLANES | SEATTLE | WA |
| 0WA6 | STEVENS MEMORIAL HOSPITAL | EDMONDS | WA |
| 0WA8 | CHILDRENS HOSPITAL EMERGENCY | SEATTLE | WA |
| 1S0 | PIERCE COUNTY - THUN FIELD | PUYALLUP | WA |
| 1WA1 | WEBER POINT | REDMOND | WA |
| 1WA6 | FALL CITY | FALL CITY | WA |
| 1WA8 | MADIGAN HOSPITAL | FORT LEWIS | WA |
| 23WA | BCAG - FREDERICKSON | PUYALLUP | WA |
| 29WA | CROSSINGS | TACOMA | WA |
| 2S1 | VASHON MUNI | VASHON | WA |
| 2WA2 | QUARTERMASTER HARBOR | DOCKTON | WA |
| 2WA4 | MOSS FIELD | GRAHAM | WA |
| 31WA | MARY BRIDGE | TACOMA | WA |
| 3B8 | SHADY ACRES | SPANAWAY | WA |
| 3WA6 | BOEING KENT | KENT | WA |
| 3WA7 | KENT BENAROYA | KENT | WA |
| 43WA | WILSON | WOODINVILLE | WA |
| 47WA | FITZ PAD 1 | WOODINVILLE | WA |
| 51WA | EVERGREEN SKY RANCH | BLACK DIAMOND | WA |
| 54WA | TUKWILA OPERATIONS CENTER | TUKWILA | WA |
| 60WA | J. J. H. | AUBURN | WA |
| 64WA | TAYMAR | BELLEVUE | WA |
| 71WA | I-90/BELLEVUE BUSI PK BOEING COMP SVCS H | BELLEVUE | WA |
| 7WA8 | GOOD SAMARITAN HOSP | PUYALLUP | WA |
| 81WA | JOBE SKIS PLANT 1 | REDMOND | WA |
| 83Q | PORT OF POULSBO MARINA MOORAGE | POULSBO | WA |
| 88WA | PERSONAL 500 SALES CO. | SUMNER | WA |
| 8WA2 | BOEING RENTON RAMP SITE NR 2 | RENTON | WA |
| 8WA3 | VALLEY MEDICAL CENTER | RENTON | WA |
| 8WA8 | SNOQUALMIE VALLEY HOSPITAL EMERGENCY ROOM | KING COUNTY | WA |
| 8WA9 | BROADCAST HOUSE HELISTOP | SEATTLE | WA |
| 92WA | CONNER | ISSAQUAH | WA |
| 95WA | BLACK DIAMOND | BLACK DIAMOND | WA |
| 9WA0 | BOEING PLANT 2 | SEATTLE | WA |
| 9WA6 | PUGET SOUND PLAZA | SEATTLE | WA |
| 9WA9 | NAVAL SUBMARINE BASE BANGOR | SILVERDALE | WA |
| BFI | BOEING FIELD/KING COUNTY INTL | SEATTLE | WA |
| PWT | BREMERTON NATIONAL | BREMERTON | WA |
| RNT | RENTON MUNI | RENTON | WA |
| S36 | CREST AIRPARK | KENT | WA |
| S37 | CLOVER PARK TECHNICAL COLLEGE | TACOMA | WA |
| S42 | APEX AIRPARK | SILVERDALE | WA |
| S44 | SPANAWAY | SPANAWAY | WA |
| S50 | AUBURN MUNI | AUBURN | WA |
| S60 | KENMORE AIR HARBOR INC | KENMORE | WA |
| TCM | MCCHORD AFB | TACOMA | WA |
| TIW | TACOMA NARROWS | TACOMA | WA |
| W36 | WILL ROGERS WILEY POST MEML | RENTON | WA |
| W37 | AMERICAN LAKE | TACOMA | WA |
| W55 | KENMORE AIR HARBOR | SEATTLE | WA |
| WA06 | DON JOHNSON HOME | AUBURN | WA |
| WA11 | BOEING MILITARY AIRPLANES | TUKWILA | WA |
| WA19 | BERKLEY STRUCTURES | REDMOND | WA |
| WA28 | TOM MATSON | AUBURN | WA |
| WA53 | HARBORVIEW MEDICAL CENTER | SEATTLE | WA |
| WA54 | 1001 FOURTH AVENUE PLAZA | SEATTLE | WA |
| WA55 | ELLIOTT PARK | SEATTLE | WA |
| WA69 | WAX ORCHARDS | VASHON | WA |
| WA75 | FLYING 'O' RANCH | COVINGTON | WA |
| WA77 | ENUMCLAW | ENUMCLAW | WA |
| WA84 | AUBURN ACADEMY | AUBURN | WA |
| WA85 | WEYERHAEUSER | AUBURN | WA |
| WA86 | BOEING - AUBURN COMPLEX | AUBURN | WA |
| WA92 | MC NEIL ISLAND EMERGENCY PAD | STEILACOOM | WA |
| WA94 | WASHINGTON AIR MUSEUM | BLACK DIAMOND | WA |
| WA96 | LEISURELAND AIRPARK | BREMERTON | WA |
| WN01 | SEATTLE PRIVATE NUMBER ONE | SEATTLE | WA |
| WN13 | VAUGHAN RANCH AIRFIELD | PORT ORCHARD | WA |
| WN16 | KOMO TV | SEATTLE | WA |
| WN19 | GIG HARBOR | GIG HARBOR | WA |
| WN22 | LAKE UNION | SEATTLE | WA |
| WN42 | FLYING H RANCH | BUCKLEY | WA |
| WN50 | ST JOSEPH HOSPITAL | TACOMA | WA |
| WN62 | AUBURN FIRE DEPARTMENT | AUBURN | WA |
| WN71 | EVANS | BELLEVUE | WA |
| WN76 | BERGSETH FIELD | ENUMCLAW | WA |
| WN79 | HALEY | WINSLOW | WA |
| WN83 | TELEPHONE UTILITIES/TIW/ | GIG HARBOR | WA |
| WN87 | BRYAN | ENUMCLAW | WA |
| WN91 | EVANS | REDMOND | WA |
| WN93 | PARK 90 | SEATTLE | WA |
| WN96 | MISTY ISLE FARMS | VASHON ISLAND | WA |

### Limitations

- Investigation has shown that some double-counting of proximate facilities exists within the 121 airport list.  For example, the list of proximate facilities for SEA includes BFI, and visa versa.

- Final evaluation and certification of service provided to proximate facilities, if any, is to be determined by the FAA.

## Appendix I:           LAAS Benefits Analysis Assumptions

This following list of assumptions was developed, prior to the start of this analysis, through a series of meetings between IBM and the FAA.  Several of these assumptions have been modified or updated during the course of this study as a result of new guidance from the FAA (e.g., #3, 4, 6, 13).

One key assumption regarding airline WAAS equipage (#20) is bounded in this study, as shown in the LAAS benefit tables, by estimating LAAS benefits for two cases:

“0% WAAS” 		– Assuming no WAAS equipage by users

“100% WAAS” 	– Assuming full WAAS equipage by users

Table I1.  LAAS Benefits Analysis Assumptions

| No. | Assumption |
| --- | --- |
| 1 | LAAS will accrue benefit only when and where it provides capabilities above and beyond those provided by other systems. |
| 2 | Where LAAS provides capabilities above and beyond those provided by other systems, it may reduce flight disruptions, including: – Diversions – Cancellations – Delays (Ground Delay Program and circular holding delays) |
| 3 | LAAS Cat-I Initial Operational Capability (IOC) at end of FY06 (changed to FY09; 2/26/04) |
| 4 | LAAS Cat-II/III IOC in FY10 (changed to FY13; 2/26/04) |
| 5 | LAAS may be installed at a maximum rate of 2 per month (24/yr), with a cap equal to the number of FAA LAAS airports to be studied |
| 6 | LAAS approach procedures, including complex procedures, will be available at commissioning of each site, for all weather conditions. (changed to 4 months after commissioning; 2/26/04) |
| 7 | LAAS training will keep pace with LAAS procedure development and publication. |
| 8 | Appropriate infrastructure will exist at LAAS candidate runways at the time of LAAS installation |
| 9 | There may be some decommissioning of ground-based navaids (consistent with the Navigation and Landing Transition Strategy) |
| 10 | LAAS provides no operational improvement during weather conditions that would be likely to close the airport. |
| 11 | LAAS, coupled with other technologies, may provide operational improvement in extremely low visibility conditions. |
| 12 | WAAS LNAV/VNAV and LPV approach procedures, including complex procedures, will be available at or before LAAS commissioning at each site. |
| 13 | WAAS Cat-I requires GPS L5 and modifications to the current architecture, and may not be achieved during the time period under study (2005 – 2024) (changed to 2009 – 2028; 2/26/04). |
| 14 | GPS L5 frequency will become operationally available after 2015 |
| 15 | Detailed study of quantitative DoD benefits are beyond the scope of this benefits analysis. |
| 16 | Assume LAAS can be sited at every airport. If all runway ends at the airport are within 5 nm* of each other, assume that one (1) LAAS will cover every runway end. Otherwise, assume that two (2) LAAS are required. (*Note: DEN is the only airport in this study that meets this criterion) |
| 17 | If any navigation system performance assumptions stated herein (SOW) cannot be achieved at a specific location, then the actual performance parameters will be used. |

| No. | Assumption |
| --- | --- |
| 18a | RNAV and RNP operations (approaches) intercept a straight-in approach at or above 500’ HAT. The straight-in approach can be supported by ILS, LAAS, or WAAS, to the appropriate operating minima. RNAV and RNP departures and missed approaches have a straight-ahead segment to at least 400’ HAT. Typical required performance (above 500’ HAT on approach, above 400’ HAT on missed approach or departure) is RNP-0.1. |
| 18b | GPS/INS, GPS/WAAS and GPS/LAAS all provide an RNP-0.1 capability, with potentially different levels of service availability |
| 18c | Cat I: The Cat I LAAS should obtain the benefits accruing from: 1) the reduction in weather minima below those supported by other systems 2) greater availability, where demonstrated. |
| 18d | Cat I: LAAS performance would generally achieve Cat I GLS with [0.99999] availability |
| 19a | Cat II/III: The Cat II/III LAAS should obtain the benefits accruing from: 1) the reduction in weather minima below those supported by other systems 2) greater availability, where demonstrated. |
| 19b | The benefits analysis does not include any decommissioning of Cat II/III ILS facilities |
| 20 | The initial airline equipage assumption is that all users equip with GPS/WAAS LPV as the baseline. The final airline equipage assumption will be based on the airline benefit assessment. |
| 21 | For efficiency analyses, expected LAAS user groups include: High-end GA (corporate turbine; helicopters), and commercial (airline and air-taxi) operators. Low-end (recreational) GA operators are not among the expected users of LAAS and will not be addressed in this efficiency analysis |
| 22 | Navigation capabilities baseline will include: NAS Baseline User Baseline Current Systems ILS X X_____________________________ WAAS-LPV X X_____________________________ VOR X X_____________________________ DME X X_____________________________ GPS X X_____________________________ Loran X X_____________________________ NDB X X_____________________________ INS X_____________________________ FMS X_____________________________ PRM X _____________________________ Multilateration X _____________________________ TAWS X_____________________________ HUD X_____________________________ |
| 23 | Navigation capabilities baseline will include: NAS Baseline User Baseline Planned Systems WAAS-GLS X X_____________________________ GPS L5 X X_____________________________ GPS – III X X_____________________________ ASDE-X X _____________________________. ADS-B X X_____________________________ CDTI X_____________________________ |
| 24 | LAAS improves safety by providing vertical guidance |
| 25 | LAAS may be a source of positioning information for surface navigation systems |
| 26 | For safety analyses covering operations in Alaska, low-end GA users, in addition to high-end GA and commercial users, will be considered. |

## Appendix J:           LAAS Efficiency Benefits by User Group

Table J1: Discounted 20 Year LAAS Operating Cost Benefits – 0% Waas Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Major Passenger Airlines | Regional Passenger Airlines | Cargo Carriers | Corporate Jet GA Operators | Other GA Operators |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $2,374,000 | 73 | $1,859,000 | $287,000 | $192,000 | $36,000 | $0 |
| ACK | $7,637,000 | 28 | $0 | $6,887,000 | $196,000 | $554,000 | $0 |
| AFW | $149,000 | 116 | $0 | $0 | $139,000 | $10,000 | $0 |
| ALB | $8,502,000 | 24 | $4,630,000 | $3,054,000 | $609,000 | $209,000 | $0 |
| ANC | $8,319,000 | 25 | $3,890,000 | $0 | $3,062,000 | $95,000 | $1,272,000 |
| ATL | $13,200,000 | 11 | $11,310,000 | $1,600,000 | $262,000 | $28,000 | $0 |
| AUS | $3,149,000 | 59 | $2,944,000 | $48,000 | $0 | $157,000 | $0 |
| AVL | $740,000 | 95 | $230,000 | $303,000 | $2,000 | $205,000 | $0 |
| BDL | $10,191,000 | 18 | $7,293,000 | $1,678,000 | $888,000 | $332,000 | $0 |
| BFI | $542,000 | 101 | $0 | $22,000 | $194,000 | $326,000 | $0 |
| BGR | $345,000 | 109 | $0 | $264,000 | $33,000 | $48,000 | $0 |
| BHM | $6,020,000 | 34 | $4,323,000 | $965,000 | $293,000 | $439,000 | $0 |
| BNA | $2,193,000 | 76 | $1,723,000 | $336,000 | $84,000 | $50,000 | $0 |
| BOI | $2,521,000 | 70 | $1,509,000 | $752,000 | $174,000 | $86,000 | $0 |
| BOS | $10,483,000 | 17 | $7,324,000 | $2,805,000 | $245,000 | $109,000 | $0 |
| BUF | $4,827,000 | 45 | $3,058,000 | $1,347,000 | $213,000 | $209,000 | $0 |
| BUR | $20,777,000 | 7 | $19,996,000 | $130,000 | $399,000 | $252,000 | $0 |
| BWI | $5,106,000 | 42 | $4,342,000 | $537,000 | $166,000 | $61,000 | $0 |
| CAE | $1,645,000 | 80 | $443,000 | $743,000 | $399,000 | $60,000 | $0 |
| CHA | $310,000 | 111 | $51,000 | $164,000 | $29,000 | $66,000 | $0 |
| CHS | $2,244,000 | 75 | $1,106,000 | $959,000 | $72,000 | $107,000 | $0 |
| CLE | $21,214,000 | 5 | $12,544,000 | $7,528,000 | $874,000 | $268,000 | $0 |
| CLT | $11,320,000 | 15 | $9,184,000 | $1,776,000 | $261,000 | $99,000 | $0 |
| CMH | $3,291,000 | 58 | $2,091,000 | $847,000 | $1,000 | $352,000 | $0 |
| COS | $6,251,000 | 32 | $4,734,000 | $816,000 | $292,000 | $409,000 | $0 |
| CVG | $13,032,000 | 12 | $6,225,000 | $5,682,000 | $1,071,000 | $54,000 | $0 |
| DAB | $462,000 | 104 | $223,000 | $51,000 | $0 | $188,000 | $0 |
| DAL | $2,960,000 | 63 | $1,903,000 | $91,000 | $71,000 | $895,000 | $0 |
| DAY | $2,436,000 | 71 | $1,004,000 | $783,000 | $576,000 | $73,000 | $0 |
| DCA | $27,535,000 | 3 | $23,584,000 | $3,922,000 | $0 | $29,000 | $0 |
| DEN | $14,830,000 | 10 | $12,048,000 | $2,338,000 | $407,000 | $37,000 | $0 |
| DFW | $34,071,000 | 1 | $26,584,000 | $6,221,000 | $1,242,000 | $24,000 | $0 |
| DLH | $533,000 | 102 | $155,000 | $147,000 | $20,000 | $211,000 | $0 |
| DSM | $1,227,000 | 86 | $490,000 | $454,000 | $214,000 | $69,000 | $0 |
| DTW | $29,190,000 | 2 | $23,100,000 | $5,486,000 | $476,000 | $128,000 | $0 |
| DVT | $4,000 | 121 | $0 | $0 | $0 | $4,000 | $0 |
| ELP | $84,000 | 118 | $71,000 | $0 | $6,000 | $7,000 | $0 |
| EUG | $2,596,000 | 67 | $592,000 | $1,243,000 | $513,000 | $248,000 | $0 |
| EWR | $9,749,000 | 20 | $7,670,000 | $1,331,000 | $694,000 | $54,000 | $0 |
| EYW | $279,000 | 113 | $0 | $262,000 | $0 | $17,000 | $0 |
| FAI | $716,000 | 96 | $339,000 | $0 | $32,000 | $0 | $345,000 |
| FAT | $301,000 | 112 | $13,000 | $249,000 | $29,000 | $10,000 | $0 |
| FLL | $2,680,000 | 65 | $2,048,000 | $453,000 | $98,000 | $81,000 | $0 |
| FWA | $2,546,000 | 69 | $38,000 | $1,604,000 | $821,000 | $83,000 | $0 |
| FXE | $45,000 | 120 | $0 | $0 | $0 | $45,000 | $0 |
| GEG | $5,371,000 | 39 | $2,735,000 | $1,518,000 | $1,069,000 | $49,000 | $0 |
| GRR | $3,870,000 | 53 | $1,263,000 | $1,326,000 | $729,000 | $552,000 | $0 |
| GSO | $4,796,000 | 46 | $2,828,000 | $1,267,000 | $540,000 | $161,000 | $0 |
| GSP | $850,000 | 94 | $310,000 | $459,000 | $51,000 | $30,000 | $0 |
| HNL | $2,667,000 | 66 | $754,000 | $1,734,000 | $177,000 | $2,000 | $0 |
| HOU | $9,799,000 | 19 | $7,491,000 | $599,000 | $1,000 | $1,708,000 | $0 |
| HPN | $6,461,000 | 31 | $1,343,000 | $1,614,000 | $1,000 | $3,503,000 | $0 |
| HSV | $551,000 | 100 | $256,000 | $101,000 | $121,000 | $73,000 | $0 |
| IAD | $7,093,000 | 29 | $3,970,000 | $2,775,000 | $127,000 | $221,000 | $0 |
| IAH | $10,989,000 | 16 | $8,980,000 | $1,772,000 | $174,000 | $63,000 | $0 |
| ICT | $1,873,000 | 78 | $829,000 | $473,000 | $266,000 | $305,000 | $0 |
| ILN | $1,045,000 | 90 | $0 | $0 | $1,045,000 | $0 | $0 |
| IND | $2,835,000 | 64 | $1,344,000 | $394,000 | $996,000 | $101,000 | $0 |
| ISP | $4,098,000 | 50 | $2,225,000 | $1,708,000 | $0 | $165,000 | $0 |
| JAN | $335,000 | 110 | $208,000 | $74,000 | $31,000 | $22,000 | $0 |
| JAX | $1,779,000 | 79 | $1,373,000 | $234,000 | $116,000 | $56,000 | $0 |
| JFK | $4,525,000 | 49 | $3,356,000 | $760,000 | $379,000 | $30,000 | $0 |
| JNU | $13,021,000 | 13 | $2,595,000 | $0 | $2,469,000 | $40,000 | $7,917,000 |
| LAS | $408,000 | 106 | $392,000 | $6,000 | $0 | $10,000 | $0 |
| LAX | $6,752,000 | 30 | $5,446,000 | $1,027,000 | $240,000 | $39,000 | $0 |
| LCK | $136,000 | 117 | $0 | $0 | $136,000 | $0 | $0 |
| LGA | $20,988,000 | 6 | $16,569,000 | $4,262,000 | $0 | $157,000 | $0 |
| LGB | $5,319,000 | 41 | $3,084,000 | $92,000 | $840,000 | $1,303,000 | $0 |
| LIT | $690,000 | 97 | $334,000 | $156,000 | $25,000 | $175,000 | $0 |
| MCI | $4,001,000 | 51 | $3,063,000 | $703,000 | $210,000 | $25,000 | $0 |
| MCO | $4,722,000 | 48 | $2,966,000 | $1,445,000 | $284,000 | $27,000 | $0 |
| MDT | $1,464,000 | 85 | $661,000 | $440,000 | $269,000 | $94,000 | $0 |
| MDW | $16,086,000 | 9 | $14,364,000 | $1,570,000 | $22,000 | $130,000 | $0 |
| MEM | $8,906,000 | 23 | $4,852,000 | $1,172,000 | $2,518,000 | $364,000 | $0 |
| MHT | $7,929,000 | 27 | $5,706,000 | $1,225,000 | $914,000 | $84,000 | $0 |
| MIA | $4,985,000 | 44 | $3,628,000 | $759,000 | $543,000 | $55,000 | $0 |
| MKE | $12,902,000 | 14 | $4,248,000 | $7,026,000 | $1,311,000 | $317,000 | $0 |
| MMU | $406,000 | 107 | $0 | $0 | $0 | $406,000 | $0 |
| MSP | $6,041,000 | 33 | $5,069,000 | $859,000 | $101,000 | $12,000 | $0 |
| MSY | $5,092,000 | 43 | $4,267,000 | $483,000 | $273,000 | $69,000 | $0 |
| OAK | $1,188,000 | 88 | $825,000 | $22,000 | $295,000 | $46,000 | $0 |
| OKC | $3,858,000 | 54 | $2,613,000 | $754,000 | $325,000 | $166,000 | $0 |
| OMA | $1,115,000 | 89 | $715,000 | $178,000 | $161,000 | $61,000 | $0 |
| ONT | $364,000 | 108 | $296,000 | $11,000 | $54,000 | $3,000 | $0 |
| ORD | $23,601,000 | 4 | $19,838,000 | $3,225,000 | $477,000 | $61,000 | $0 |
| ORF | $4,754,000 | 47 | $2,925,000 | $1,273,000 | $335,000 | $221,000 | $0 |
| PBI | $1,547,000 | 84 | $941,000 | $364,000 | $40,000 | $202,000 | $0 |
| PDX | $3,080,000 | 61 | $2,117,000 | $664,000 | $235,000 | $64,000 | $0 |
| PHL | $5,771,000 | 35 | $4,282,000 | $1,023,000 | $343,000 | $123,000 | $0 |
| PHX | $3,081,000 | 60 | $2,742,000 | $137,000 | $148,000 | $54,000 | $0 |
| PIE | $501,000 | 103 | $153,000 | $0 | $76,000 | $272,000 | $0 |
| PIT | $8,132,000 | 26 | $5,814,000 | $2,074,000 | $178,000 | $66,000 | $0 |
| PVD | $5,378,000 | 38 | $2,802,000 | $1,998,000 | $283,000 | $295,000 | $0 |
| RDU | $3,931,000 | 52 | $2,117,000 | $1,552,000 | $126,000 | $136,000 | $0 |
| RFD | $1,561,000 | 83 | $0 | $71,000 | $1,273,000 | $217,000 | $0 |
| RIC | $5,525,000 | 37 | $3,239,000 | $1,563,000 | $544,000 | $179,000 | $0 |
| RNO | $2,420,000 | 72 | $2,060,000 | $138,000 | $147,000 | $75,000 | $0 |
| ROC | $1,633,000 | 81 | $657,000 | $633,000 | $243,000 | $100,000 | $0 |
| RSW | $5,611,000 | 36 | $4,387,000 | $651,000 | $117,000 | $456,000 | $0 |
| SAN | $16,784,000 | 8 | $14,383,000 | $1,728,000 | $413,000 | $260,000 | $0 |
| SAT | $2,074,000 | 77 | $1,722,000 | $22,000 | $154,000 | $176,000 | $0 |
| SDF | $560,000 | 99 | $223,000 | $60,000 | $266,000 | $11,000 | $0 |
| SEA | $9,276,000 | 21 | $6,557,000 | $2,204,000 | $497,000 | $18,000 | $0 |
| SFB | $179,000 | 115 | $0 | $80,000 | $0 | $99,000 | $0 |
| SFO | $2,253,000 | 74 | $2,006,000 | $192,000 | $32,000 | $23,000 | $0 |
| SHV | $890,000 | 93 | $58,000 | $683,000 | $86,000 | $63,000 | $0 |
| SJC | $9,197,000 | 22 | $8,347,000 | $153,000 | $379,000 | $318,000 | $0 |
| SLC | $5,344,000 | 40 | $4,251,000 | $615,000 | $259,000 | $219,000 | $0 |
| SMF | $2,975,000 | 62 | $2,488,000 | $209,000 | $240,000 | $38,000 | $0 |
| SNA | $3,459,000 | 56 | $2,498,000 | $126,000 | $74,000 | $761,000 | $0 |
| STL | $2,580,000 | 68 | $2,229,000 | $328,000 | $1,000 | $22,000 | $0 |
| SWF | $461,000 | 105 | $32,000 | $377,000 | $20,000 | $32,000 | $0 |
| SYR | $1,196,000 | 87 | $514,000 | $549,000 | $109,000 | $24,000 | $0 |
| TEB | $3,464,000 | 55 | $0 | $0 | $63,000 | $3,401,000 | $0 |
| TLH | $1,621,000 | 82 | $249,000 | $834,000 | $240,000 | $298,000 | $0 |
| TPA | $3,339,000 | 57 | $2,708,000 | $419,000 | $49,000 | $163,000 | $0 |
| TRI | $272,000 | 114 | $31,000 | $180,000 | $9,000 | $52,000 | $0 |
| TUL | $983,000 | 91 | $485,000 | $351,000 | $38,000 | $109,000 | $0 |
| TUS | $63,000 | 119 | $58,000 | $0 | $1,000 | $4,000 | $0 |
| TYS | $902,000 | 92 | $371,000 | $370,000 | $106,000 | $55,000 | $0 |
| VNY | $568,000 | 98 | $0 | $0 | $0 | $568,000 | $0 |
| Total | $638,902,000 |  | $434,913,000 | $128,009,000 | $39,763,000 | $26,683,000 | $9,534,000 |

Table J2: Discounted 20 year LAAS Passenger Time Savings – 0% Waas Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Major Passenger Airlines | Regional Passenger Airlines | Cargo Carriers | Corporate Jet GA Operators | Other GA Operators |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $2,945,000 | 69 | $2,465,000 | $473,000 | $0 | $7,000 | $0 |
| ACK | $11,477,000 | 22 | $0 | $11,379,000 | $0 | $98,000 | $0 |
| AFW | $2,000 | 118 | $0 | $0 | $0 | $2,000 | $0 |
| ALB | $11,300,000 | 23 | $6,227,000 | $5,030,000 | $0 | $43,000 | $0 |
| ANC | $5,383,000 | 49 | $4,996,000 | $0 | $0 | $17,000 | $370,000 |
| ATL | $18,415,000 | 11 | $15,806,000 | $2,603,000 | $0 | $6,000 | $0 |
| AUS | $3,959,000 | 59 | $3,850,000 | $79,000 | $0 | $30,000 | $0 |
| AVL | $885,000 | 92 | $345,000 | $493,000 | $0 | $47,000 | $0 |
| BDL | $12,216,000 | 19 | $9,384,000 | $2,772,000 | $0 | $60,000 | $0 |
| BFI | $108,000 | 113 | $0 | $36,000 | $0 | $72,000 | $0 |
| BGR | $444,000 | 101 | $0 | $435,000 | $0 | $9,000 | $0 |
| BHM | $7,221,000 | 34 | $5,548,000 | $1,595,000 | $0 | $78,000 | $0 |
| BNA | $2,776,000 | 72 | $2,211,000 | $556,000 | $0 | $9,000 | $0 |
| BOI | $3,193,000 | 65 | $1,936,000 | $1,242,000 | $0 | $15,000 | $0 |
| BOS | $14,053,000 | 16 | $9,400,000 | $4,634,000 | $0 | $19,000 | $0 |
| BUF | $6,194,000 | 40 | $3,932,000 | $2,225,000 | $0 | $37,000 | $0 |
| BUR | $26,026,000 | 7 | $25,765,000 | $214,000 | $0 | $47,000 | $0 |
| BWI | $6,471,000 | 36 | $5,573,000 | $887,000 | $0 | $11,000 | $0 |
| CAE | $1,807,000 | 81 | $569,000 | $1,227,000 | $0 | $11,000 | $0 |
| CHA | $348,000 | 107 | $66,000 | $270,000 | $0 | $12,000 | $0 |
| CHS | $3,022,000 | 67 | $1,419,000 | $1,584,000 | $0 | $19,000 | $0 |
| CLE | $28,585,000 | 5 | $16,099,000 | $12,438,000 | $0 | $48,000 | $0 |
| CLT | $14,740,000 | 14 | $11,787,000 | $2,935,000 | $0 | $18,000 | $0 |
| CMH | $4,308,000 | 57 | $2,841,000 | $1,393,000 | $0 | $74,000 | $0 |
| COS | $8,038,000 | 29 | $6,610,000 | $1,339,000 | $0 | $89,000 | $0 |
| CVG | $15,891,000 | 13 | $7,913,000 | $7,970,000 | $0 | $8,000 | $0 |
| DAB | $450,000 | 100 | $324,000 | $83,000 | $0 | $43,000 | $0 |
| DAL | $3,124,000 | 66 | $2,772,000 | $149,000 | $0 | $203,000 | $0 |
| DAY | $2,605,000 | 74 | $1,300,000 | $1,292,000 | $0 | $13,000 | $0 |
| DCA | $36,752,000 | 3 | $30,267,000 | $6,480,000 | $0 | $5,000 | $0 |
| DEN | $19,332,000 | 10 | $15,463,000 | $3,862,000 | $0 | $7,000 | $0 |
| DFW | $49,929,000 | 1 | $40,027,000 | $9,897,000 | $0 | $5,000 | $0 |
| DLH | $513,000 | 99 | $226,000 | $241,000 | $0 | $46,000 | $0 |
| DSM | $1,392,000 | 85 | $629,000 | $751,000 | $0 | $12,000 | $0 |
| DTW | $39,394,000 | 2 | $30,349,000 | $9,025,000 | $0 | $20,000 | $0 |
| DVT | $1,000 | 119 | $0 | $0 | $0 | $1,000 | $0 |
| ELP | $101,000 | 114 | $99,000 | $0 | $0 | $2,000 | $0 |
| EUG | $2,968,000 | 68 | $878,000 | $2,033,000 | $0 | $57,000 | $0 |
| EWR | $12,052,000 | 20 | $9,843,000 | $2,199,000 | $0 | $10,000 | $0 |
| EYW | $436,000 | 102 | $0 | $433,000 | $0 | $3,000 | $0 |
| FAI | $535,000 | 97 | $435,000 | $0 | $0 | $0 | $100,000 |
| FAT | $429,000 | 103 | $17,000 | $410,000 | $0 | $2,000 | $0 |
| FLL | $3,477,000 | 63 | $2,716,000 | $746,000 | $0 | $15,000 | $0 |
| FWA | $2,714,000 | 73 | $49,000 | $2,650,000 | $0 | $15,000 | $0 |
| FXE | $9,000 | 117 | $0 | $0 | $0 | $9,000 | $0 |
| GEG | $6,044,000 | 42 | $3,527,000 | $2,508,000 | $0 | $9,000 | $0 |
| GRR | $4,043,000 | 58 | $1,750,000 | $2,179,000 | $0 | $114,000 | $0 |
| GSO | $5,752,000 | 45 | $3,629,000 | $2,094,000 | $0 | $29,000 | $0 |
| GSP | $1,162,000 | 90 | $398,000 | $759,000 | $0 | $5,000 | $0 |
| HNL | $3,834,000 | 61 | $968,000 | $2,866,000 | $0 | $0 | $0 |
| HOU | $12,574,000 | 17 | $11,207,000 | $981,000 | $0 | $386,000 | $0 |
| HPN | $5,459,000 | 48 | $2,030,000 | $2,624,000 | $0 | $805,000 | $0 |
| HSV | $564,000 | 96 | $382,000 | $165,000 | $0 | $17,000 | $0 |
| IAD | $9,718,000 | 25 | $5,095,000 | $4,584,000 | $0 | $39,000 | $0 |
| IAH | $14,353,000 | 15 | $11,532,000 | $2,811,000 | $0 | $10,000 | $0 |
| ICT | $1,899,000 | 79 | $1,064,000 | $781,000 | $0 | $54,000 | $0 |
| ILN | $0 | 120 | $0 | $0 | $0 | $0 | $0 |
| IND | $2,392,000 | 75 | $1,724,000 | $650,000 | $0 | $18,000 | $0 |
| ISP | $5,974,000 | 43 | $3,133,000 | $2,807,000 | $0 | $34,000 | $0 |
| JAN | $395,000 | 105 | $268,000 | $123,000 | $0 | $4,000 | $0 |
| JAX | $2,160,000 | 77 | $1,764,000 | $386,000 | $0 | $10,000 | $0 |
| JFK | $5,555,000 | 47 | $4,294,000 | $1,256,000 | $0 | $5,000 | $0 |
| JNU | $5,671,000 | 46 | $3,357,000 | $0 | $0 | $8,000 | $2,306,000 |
| LAS | $516,000 | 98 | $505,000 | $9,000 | $0 | $2,000 | $0 |
| LAX | $8,693,000 | 27 | $6,989,000 | $1,697,000 | $0 | $7,000 | $0 |
| LCK | $0 | 121 | $0 | $0 | $0 | $0 | $0 |
| LGA | $28,334,000 | 6 | $21,264,000 | $7,042,000 | $0 | $28,000 | $0 |
| LGB | $4,579,000 | 55 | $4,215,000 | $151,000 | $0 | $213,000 | $0 |
| LIT | $740,000 | 93 | $449,000 | $258,000 | $0 | $33,000 | $0 |
| MCI | $5,096,000 | 51 | $3,931,000 | $1,161,000 | $0 | $4,000 | $0 |
| MCO | $6,414,000 | 38 | $4,037,000 | $2,372,000 | $0 | $5,000 | $0 |
| MDT | $1,665,000 | 83 | $921,000 | $723,000 | $0 | $21,000 | $0 |
| MDW | $22,049,000 | 8 | $19,439,000 | $2,584,000 | $0 | $26,000 | $0 |
| MEM | $8,143,000 | 28 | $6,163,000 | $1,932,000 | $0 | $48,000 | $0 |
| MHT | $9,579,000 | 26 | $7,542,000 | $2,020,000 | $0 | $17,000 | $0 |
| MIA | $5,921,000 | 44 | $4,657,000 | $1,254,000 | $0 | $10,000 | $0 |
| MKE | $17,122,000 | 12 | $5,469,000 | $11,599,000 | $0 | $54,000 | $0 |
| MMU | $83,000 | 115 | $0 | $0 | $0 | $83,000 | $0 |
| MSP | $7,927,000 | 30 | $6,506,000 | $1,419,000 | $0 | $2,000 | $0 |
| MSY | $6,352,000 | 39 | $5,541,000 | $798,000 | $0 | $13,000 | $0 |
| OAK | $1,194,000 | 89 | $1,148,000 | $37,000 | $0 | $9,000 | $0 |
| OKC | $4,660,000 | 54 | $3,383,000 | $1,246,000 | $0 | $31,000 | $0 |
| OMA | $1,222,000 | 86 | $918,000 | $293,000 | $0 | $11,000 | $0 |
| ONT | $398,000 | 104 | $380,000 | $18,000 | $0 | $0 | $0 |
| ORD | $30,997,000 | 4 | $25,665,000 | $5,321,000 | $0 | $11,000 | $0 |
| ORF | $6,175,000 | 41 | $4,051,000 | $2,076,000 | $0 | $48,000 | $0 |
| PBI | $1,879,000 | 80 | $1,237,000 | $602,000 | $0 | $40,000 | $0 |
| PDX | $3,911,000 | 60 | $2,804,000 | $1,095,000 | $0 | $12,000 | $0 |
| PHL | $7,399,000 | 33 | $5,695,000 | $1,681,000 | $0 | $23,000 | $0 |
| PHX | $4,442,000 | 56 | $4,207,000 | $222,000 | $0 | $13,000 | $0 |
| PIE | $265,000 | 109 | $208,000 | $0 | $0 | $57,000 | $0 |
| PIT | $10,901,000 | 24 | $7,462,000 | $3,427,000 | $0 | $12,000 | $0 |
| PVD | $7,615,000 | 32 | $4,266,000 | $3,286,000 | $0 | $63,000 | $0 |
| RDU | $5,302,000 | 50 | $2,715,000 | $2,564,000 | $0 | $23,000 | $0 |
| RFD | $163,000 | 110 | $0 | $116,000 | $0 | $47,000 | $0 |
| RIC | $6,786,000 | 35 | $4,178,000 | $2,575,000 | $0 | $33,000 | $0 |
| RNO | $2,911,000 | 70 | $2,668,000 | $229,000 | $0 | $14,000 | $0 |
| ROC | $2,026,000 | 78 | $994,000 | $1,012,000 | $0 | $20,000 | $0 |
| RSW | $7,756,000 | 31 | $6,590,000 | $1,061,000 | $0 | $105,000 | $0 |
| SAN | $21,360,000 | 9 | $18,459,000 | $2,855,000 | $0 | $46,000 | $0 |
| SAT | $2,331,000 | 76 | $2,260,000 | $37,000 | $0 | $34,000 | $0 |
| SDF | $387,000 | 106 | $286,000 | $99,000 | $0 | $2,000 | $0 |
| SEA | $12,268,000 | 18 | $8,764,000 | $3,501,000 | $0 | $3,000 | $0 |
| SFB | $153,000 | 111 | $0 | $132,000 | $0 | $21,000 | $0 |
| SFO | $2,908,000 | 71 | $2,586,000 | $318,000 | $0 | $4,000 | $0 |
| SHV | $1,214,000 | 88 | $74,000 | $1,129,000 | $0 | $11,000 | $0 |
| SJC | $11,882,000 | 21 | $11,562,000 | $252,000 | $0 | $68,000 | $0 |
| SLC | $6,425,000 | 37 | $5,380,000 | $1,016,000 | $0 | $29,000 | $0 |
| SMF | $3,651,000 | 62 | $3,299,000 | $344,000 | $0 | $8,000 | $0 |
| SNA | $4,759,000 | 52 | $4,384,000 | $202,000 | $0 | $173,000 | $0 |
| STL | $3,407,000 | 64 | $2,862,000 | $541,000 | $0 | $4,000 | $0 |
| SWF | $670,000 | 94 | $42,000 | $622,000 | $0 | $6,000 | $0 |
| SYR | $1,572,000 | 84 | $660,000 | $908,000 | $0 | $4,000 | $0 |
| TEB | $653,000 | 95 | $0 | $0 | $0 | $653,000 | $0 |
| TLH | $1,799,000 | 82 | $368,000 | $1,363,000 | $0 | $68,000 | $0 |
| TPA | $4,707,000 | 53 | $3,986,000 | $684,000 | $0 | $37,000 | $0 |
| TRI | $346,000 | 108 | $39,000 | $298,000 | $0 | $9,000 | $0 |
| TUL | $1,221,000 | 87 | $623,000 | $579,000 | $0 | $19,000 | $0 |
| TUS | $78,000 | 116 | $77,000 | $0 | $0 | $1,000 | $0 |
| TYS | $1,098,000 | 91 | $476,000 | $612,000 | $0 | $10,000 | $0 |
| VNY | $112,000 | 112 | $0 | $0 | $0 | $112,000 | $0 |
| Total | $795,785,000 |  | $578,642,000 | $209,006,000 | $0 | $5,361,000 | $2,776,000 |

Table J3: Discounted 20 year LAAS operating cost Benefits – 100% Waas Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Major Passenger Airlines | Regional Passenger Airlines | Cargo Carriers | Corporate Jet GA Operators | Other GA Operators |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $1,131,000 | 74 | $873,000 | $129,000 | $106,000 | $23,000 | $0 |
| ACK | $7,637,000 | 16 | $0 | $6,887,000 | $196,000 | $554,000 | $0 |
| AFW | $149,000 | 112 | $0 | $0 | $139,000 | $10,000 | $0 |
| ALB | $5,382,000 | 25 | $2,937,000 | $1,861,000 | $423,000 | $161,000 | $0 |
| ANC | $4,619,000 | 33 | $2,254,000 | $0 | $1,778,000 | $55,000 | $532,000 |
| ATL | $11,922,000 | 7 | $10,275,000 | $1,403,000 | $221,000 | $23,000 | $0 |
| AUS | $3,149,000 | 46 | $2,944,000 | $48,000 | $0 | $157,000 | $0 |
| AVL | $740,000 | 86 | $230,000 | $303,000 | $2,000 | $205,000 | $0 |
| BDL | $3,510,000 | 42 | $2,503,000 | $570,000 | $315,000 | $122,000 | $0 |
| BFI | $542,000 | 94 | $0 | $22,000 | $194,000 | $326,000 | $0 |
| BGR | $345,000 | 103 | $0 | $264,000 | $33,000 | $48,000 | $0 |
| BHM | $386,000 | 100 | $297,000 | $58,000 | $0 | $31,000 | $0 |
| BNA | $1,141,000 | 73 | $983,000 | $105,000 | $21,000 | $32,000 | $0 |
| BOI | $2,521,000 | 59 | $1,509,000 | $752,000 | $174,000 | $86,000 | $0 |
| BOS | $10,483,000 | 10 | $7,324,000 | $2,805,000 | $245,000 | $109,000 | $0 |
| BUF | $4,517,000 | 34 | $3,058,000 | $1,165,000 | $181,000 | $113,000 | $0 |
| BUR | $587,000 | 90 | $464,000 | $10,000 | $29,000 | $84,000 | $0 |
| BWI | $5,106,000 | 26 | $4,342,000 | $537,000 | $166,000 | $61,000 | $0 |
| CAE | $1,021,000 | 79 | $283,000 | $455,000 | $245,000 | $38,000 | $0 |
| CHA | $290,000 | 108 | $51,000 | $164,000 | $29,000 | $46,000 | $0 |
| CHS | $1,273,000 | 70 | $630,000 | $545,000 | $38,000 | $60,000 | $0 |
| CLE | $4,949,000 | 29 | $2,761,000 | $1,921,000 | $190,000 | $77,000 | $0 |
| CLT | $11,320,000 | 8 | $9,184,000 | $1,776,000 | $261,000 | $99,000 | $0 |
| CMH | $3,291,000 | 45 | $2,091,000 | $847,000 | $1,000 | $352,000 | $0 |
| COS | $4,999,000 | 28 | $3,754,000 | $624,000 | $254,000 | $367,000 | $0 |
| CVG | $9,628,000 | 12 | $4,825,000 | $4,060,000 | $709,000 | $34,000 | $0 |
| DAB | $462,000 | 98 | $223,000 | $51,000 | $0 | $188,000 | $0 |
| DAL | $2,960,000 | 53 | $1,903,000 | $91,000 | $71,000 | $895,000 | $0 |
| DAY | $1,307,000 | 69 | $579,000 | $385,000 | $300,000 | $43,000 | $0 |
| DCA | $2,762,000 | 56 | $2,356,000 | $403,000 | $0 | $3,000 | $0 |
| DEN | $14,830,000 | 4 | $12,048,000 | $2,338,000 | $407,000 | $37,000 | $0 |
| DFW | $21,031,000 | 2 | $16,906,000 | $3,490,000 | $624,000 | $11,000 | $0 |
| DLH | $511,000 | 96 | $155,000 | $147,000 | $20,000 | $189,000 | $0 |
| DSM | $1,227,000 | 72 | $490,000 | $454,000 | $214,000 | $69,000 | $0 |
| DTW | $13,288,000 | 6 | $10,904,000 | $2,119,000 | $217,000 | $48,000 | $0 |
| DVT | $0 | 121 | $0 | $0 | $0 | $0 | $0 |
| ELP | $84,000 | 116 | $71,000 | $0 | $6,000 | $7,000 | $0 |
| EUG | $2,021,000 | 64 | $501,000 | $817,000 | $463,000 | $240,000 | $0 |
| EWR | $9,749,000 | 11 | $7,670,000 | $1,331,000 | $694,000 | $54,000 | $0 |
| EYW | $70,000 | 117 | $0 | $62,000 | $0 | $8,000 | $0 |
| FAI | $474,000 | 97 | $339,000 | $0 | $32,000 | $0 | $103,000 |
| FAT | $301,000 | 107 | $13,000 | $249,000 | $29,000 | $10,000 | $0 |
| FLL | $2,306,000 | 60 | $1,734,000 | $415,000 | $98,000 | $59,000 | $0 |
| FWA | $518,000 | 95 | $12,000 | $270,000 | $193,000 | $43,000 | $0 |
| FXE | $24,000 | 120 | $0 | $0 | $0 | $24,000 | $0 |
| GEG | $3,404,000 | 43 | $2,001,000 | $740,000 | $623,000 | $40,000 | $0 |
| GRR | $3,516,000 | 41 | $1,263,000 | $1,209,000 | $599,000 | $445,000 | $0 |
| GSO | $4,796,000 | 30 | $2,828,000 | $1,267,000 | $540,000 | $161,000 | $0 |
| GSP | $850,000 | 83 | $310,000 | $459,000 | $51,000 | $30,000 | $0 |
| HNL | $105,000 | 115 | $20,000 | $85,000 | $0 | $0 | $0 |
| HOU | $9,495,000 | 13 | $7,491,000 | $367,000 | $1,000 | $1,636,000 | $0 |
| HPN | $6,308,000 | 20 | $1,312,000 | $1,544,000 | $1,000 | $3,451,000 | $0 |
| HSV | $551,000 | 93 | $256,000 | $101,000 | $121,000 | $73,000 | $0 |
| IAD | $7,093,000 | 17 | $3,970,000 | $2,775,000 | $127,000 | $221,000 | $0 |
| IAH | $10,989,000 | 9 | $8,980,000 | $1,772,000 | $174,000 | $63,000 | $0 |
| ICT | $1,092,000 | 76 | $515,000 | $246,000 | $136,000 | $195,000 | $0 |
| ILN | $1,045,000 | 78 | $0 | $0 | $1,045,000 | $0 | $0 |
| IND | $2,835,000 | 55 | $1,344,000 | $394,000 | $996,000 | $101,000 | $0 |
| ISP | $3,727,000 | 40 | $2,225,000 | $1,375,000 | $0 | $127,000 | $0 |
| JAN | $335,000 | 105 | $208,000 | $74,000 | $31,000 | $22,000 | $0 |
| JAX | $1,779,000 | 66 | $1,373,000 | $234,000 | $116,000 | $56,000 | $0 |
| JFK | $4,269,000 | 36 | $3,109,000 | $760,000 | $379,000 | $21,000 | $0 |
| JNU | $411,000 | 99 | $236,000 | $0 | $74,000 | $15,000 | $86,000 |
| LAS | $32,000 | 118 | $31,000 | $0 | $0 | $1,000 | $0 |
| LAX | $6,752,000 | 18 | $5,446,000 | $1,027,000 | $240,000 | $39,000 | $0 |
| LCK | $136,000 | 113 | $0 | $0 | $136,000 | $0 | $0 |
| LGA | $13,568,000 | 5 | $10,712,000 | $2,755,000 | $0 | $101,000 | $0 |
| LGB | $2,648,000 | 57 | $1,305,000 | $65,000 | $649,000 | $629,000 | $0 |
| LIT | $552,000 | 92 | $334,000 | $107,000 | $25,000 | $86,000 | $0 |
| MCI | $4,001,000 | 37 | $3,063,000 | $703,000 | $210,000 | $25,000 | $0 |
| MCO | $3,065,000 | 50 | $2,300,000 | $591,000 | $152,000 | $22,000 | $0 |
| MDT | $1,464,000 | 68 | $661,000 | $440,000 | $269,000 | $94,000 | $0 |
| MDW | $16,034,000 | 3 | $14,364,000 | $1,570,000 | $22,000 | $78,000 | $0 |
| MEM | $6,430,000 | 19 | $2,810,000 | $1,125,000 | $2,381,000 | $114,000 | $0 |
| MHT | $6,213,000 | 21 | $4,453,000 | $945,000 | $743,000 | $72,000 | $0 |
| MIA | $3,083,000 | 48 | $2,267,000 | $462,000 | $320,000 | $34,000 | $0 |
| MKE | $5,060,000 | 27 | $1,631,000 | $2,786,000 | $528,000 | $115,000 | $0 |
| MMU | $264,000 | 109 | $0 | $0 | $0 | $264,000 | $0 |
| MSP | $6,041,000 | 22 | $5,069,000 | $859,000 | $101,000 | $12,000 | $0 |
| MSY | $2,896,000 | 54 | $2,600,000 | $146,000 | $99,000 | $51,000 | $0 |
| OAK | $1,079,000 | 77 | $825,000 | $6,000 | $215,000 | $33,000 | $0 |
| OKC | $2,222,000 | 62 | $1,616,000 | $325,000 | $166,000 | $115,000 | $0 |
| OMA | $1,115,000 | 75 | $715,000 | $178,000 | $161,000 | $61,000 | $0 |
| ONT | $364,000 | 101 | $296,000 | $11,000 | $54,000 | $3,000 | $0 |
| ORD | $23,601,000 | 1 | $19,838,000 | $3,225,000 | $477,000 | $61,000 | $0 |
| ORF | $4,701,000 | 32 | $2,899,000 | $1,253,000 | $330,000 | $219,000 | $0 |
| PBI | $780,000 | 85 | $527,000 | $98,000 | $6,000 | $149,000 | $0 |
| PDX | $3,030,000 | 51 | $2,072,000 | $664,000 | $235,000 | $59,000 | $0 |
| PHL | $5,771,000 | 23 | $4,282,000 | $1,023,000 | $343,000 | $123,000 | $0 |
| PHX | $3,081,000 | 49 | $2,742,000 | $137,000 | $148,000 | $54,000 | $0 |
| PIE | $353,000 | 102 | $100,000 | $0 | $59,000 | $194,000 | $0 |
| PIT | $8,132,000 | 15 | $5,814,000 | $2,074,000 | $178,000 | $66,000 | $0 |
| PVD | $4,347,000 | 35 | $2,802,000 | $1,078,000 | $237,000 | $230,000 | $0 |
| RDU | $3,873,000 | 38 | $2,073,000 | $1,552,000 | $126,000 | $122,000 | $0 |
| RFD | $852,000 | 82 | $0 | $20,000 | $666,000 | $166,000 | $0 |
| RIC | $3,134,000 | 47 | $1,838,000 | $874,000 | $315,000 | $107,000 | $0 |
| RNO | $597,000 | 89 | $509,000 | $31,000 | $32,000 | $25,000 | $0 |
| ROC | $992,000 | 80 | $440,000 | $374,000 | $122,000 | $56,000 | $0 |
| RSW | $5,611,000 | 24 | $4,387,000 | $651,000 | $117,000 | $456,000 | $0 |
| SAN | $672,000 | 88 | $576,000 | $67,000 | $19,000 | $10,000 | $0 |
| SAT | $2,074,000 | 63 | $1,722,000 | $22,000 | $154,000 | $176,000 | $0 |
| SDF | $560,000 | 91 | $223,000 | $60,000 | $266,000 | $11,000 | $0 |
| SEA | $8,761,000 | 14 | $6,236,000 | $2,055,000 | $454,000 | $16,000 | $0 |
| SFB | $172,000 | 111 | $0 | $80,000 | $0 | $92,000 | $0 |
| SFO | $2,253,000 | 61 | $2,006,000 | $192,000 | $32,000 | $23,000 | $0 |
| SHV | $342,000 | 104 | $58,000 | $217,000 | $41,000 | $26,000 | $0 |
| SJC | $4,718,000 | 31 | $4,208,000 | $54,000 | $225,000 | $231,000 | $0 |
| SLC | $3,811,000 | 39 | $2,857,000 | $615,000 | $259,000 | $80,000 | $0 |
| SMF | $2,975,000 | 52 | $2,488,000 | $209,000 | $240,000 | $38,000 | $0 |
| SNA | $3,352,000 | 44 | $2,498,000 | $98,000 | $74,000 | $682,000 | $0 |
| STL | $2,580,000 | 58 | $2,229,000 | $328,000 | $1,000 | $22,000 | $0 |
| SWF | $130,000 | 114 | $32,000 | $71,000 | $3,000 | $24,000 | $0 |
| SYR | $784,000 | 84 | $384,000 | $323,000 | $59,000 | $18,000 | $0 |
| TEB | $1,264,000 | 71 | $0 | $0 | $14,000 | $1,250,000 | $0 |
| TLH | $1,621,000 | 67 | $249,000 | $834,000 | $240,000 | $298,000 | $0 |
| TPA | $2,002,000 | 65 | $1,609,000 | $202,000 | $49,000 | $142,000 | $0 |
| TRI | $220,000 | 110 | $31,000 | $152,000 | $9,000 | $28,000 | $0 |
| TUL | $710,000 | 87 | $485,000 | $146,000 | $21,000 | $58,000 | $0 |
| TUS | $29,000 | 119 | $24,000 | $0 | $1,000 | $4,000 | $0 |
| TYS | $902,000 | 81 | $371,000 | $370,000 | $106,000 | $55,000 | $0 |
| VNY | $334,000 | 106 | $0 | $0 | $0 | $334,000 | $0 |
| Total | $429,303,000 |  | $296,024,000 | $86,585,000 | $26,461,000 | $19,512,000 | $721,000 |

Table J4: Discounted 20 year LAAS Passenger Time Savings – 100% Waas Equipage Scenario, by Airport

| Airport | Total Benefit | Rank by Total Benefit | Major Passenger Airlines | Regional Passenger Airlines | Cargo Carriers | Corporate Jet GA Operators | Other GA Operators |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ABQ | $1,417,000 | 71 | $1,200,000 | $212,000 | $0 | $5,000 | $0 |
| ACK | $11,477,000 | 15 | $0 | $11,379,000 | $0 | $98,000 | $0 |
| AFW | $2,000 | 118 | $0 | $0 | $0 | $2,000 | $0 |
| ALB | $7,147,000 | 23 | $4,054,000 | $3,058,000 | $0 | $35,000 | $0 |
| ANC | $3,061,000 | 57 | $2,896,000 | $0 | $0 | $10,000 | $155,000 |
| ATL | $16,289,000 | 7 | $13,990,000 | $2,294,000 | $0 | $5,000 | $0 |
| AUS | $3,959,000 | 45 | $3,850,000 | $79,000 | $0 | $30,000 | $0 |
| AVL | $885,000 | 83 | $345,000 | $493,000 | $0 | $47,000 | $0 |
| BDL | $4,200,000 | 43 | $3,237,000 | $941,000 | $0 | $22,000 | $0 |
| BFI | $108,000 | 109 | $0 | $36,000 | $0 | $72,000 | $0 |
| BGR | $444,000 | 95 | $0 | $435,000 | $0 | $9,000 | $0 |
| BHM | $482,000 | 91 | $381,000 | $95,000 | $0 | $6,000 | $0 |
| BNA | $1,442,000 | 70 | $1,262,000 | $174,000 | $0 | $6,000 | $0 |
| BOI | $3,193,000 | 55 | $1,936,000 | $1,242,000 | $0 | $15,000 | $0 |
| BOS | $14,053,000 | 10 | $9,400,000 | $4,634,000 | $0 | $19,000 | $0 |
| BUF | $5,877,000 | 31 | $3,932,000 | $1,925,000 | $0 | $20,000 | $0 |
| BUR | $732,000 | 87 | $698,000 | $16,000 | $0 | $18,000 | $0 |
| BWI | $6,471,000 | 26 | $5,573,000 | $887,000 | $0 | $11,000 | $0 |
| CAE | $1,121,000 | 78 | $363,000 | $751,000 | $0 | $7,000 | $0 |
| CHA | $344,000 | 102 | $66,000 | $270,000 | $0 | $8,000 | $0 |
| CHS | $1,721,000 | 68 | $809,000 | $901,000 | $0 | $11,000 | $0 |
| CLE | $6,730,000 | 25 | $3,543,000 | $3,173,000 | $0 | $14,000 | $0 |
| CLT | $14,740,000 | 8 | $11,787,000 | $2,935,000 | $0 | $18,000 | $0 |
| CMH | $4,308,000 | 42 | $2,841,000 | $1,393,000 | $0 | $74,000 | $0 |
| COS | $6,457,000 | 27 | $5,352,000 | $1,023,000 | $0 | $82,000 | $0 |
| CVG | $12,294,000 | 11 | $6,151,000 | $6,138,000 | $0 | $5,000 | $0 |
| DAB | $450,000 | 94 | $324,000 | $83,000 | $0 | $43,000 | $0 |
| DAL | $3,124,000 | 56 | $2,772,000 | $149,000 | $0 | $203,000 | $0 |
| DAY | $1,397,000 | 72 | $754,000 | $635,000 | $0 | $8,000 | $0 |
| DCA | $3,690,000 | 50 | $3,024,000 | $666,000 | $0 | $0 | $0 |
| DEN | $19,332,000 | 4 | $15,463,000 | $3,862,000 | $0 | $7,000 | $0 |
| DFW | $28,953,000 | 2 | $23,293,000 | $5,658,000 | $0 | $2,000 | $0 |
| DLH | $509,000 | 90 | $226,000 | $241,000 | $0 | $42,000 | $0 |
| DSM | $1,392,000 | 73 | $629,000 | $751,000 | $0 | $12,000 | $0 |
| DTW | $18,350,000 | 5 | $14,879,000 | $3,463,000 | $0 | $8,000 | $0 |
| DVT | $0 | 119 | $0 | $0 | $0 | $0 | $0 |
| ELP | $101,000 | 111 | $99,000 | $0 | $0 | $2,000 | $0 |
| EUG | $2,146,000 | 66 | $762,000 | $1,329,000 | $0 | $55,000 | $0 |
| EWR | $12,052,000 | 13 | $9,843,000 | $2,199,000 | $0 | $10,000 | $0 |
| EYW | $104,000 | 110 | $0 | $103,000 | $0 | $1,000 | $0 |
| FAI | $465,000 | 93 | $435,000 | $0 | $0 | $0 | $30,000 |
| FAT | $429,000 | 97 | $17,000 | $410,000 | $0 | $2,000 | $0 |
| FLL | $3,018,000 | 58 | $2,322,000 | $684,000 | $0 | $12,000 | $0 |
| FWA | $470,000 | 92 | $16,000 | $446,000 | $0 | $8,000 | $0 |
| FXE | $5,000 | 117 | $0 | $0 | $0 | $5,000 | $0 |
| GEG | $3,814,000 | 49 | $2,584,000 | $1,223,000 | $0 | $7,000 | $0 |
| GRR | $3,832,000 | 48 | $1,750,000 | $1,987,000 | $0 | $95,000 | $0 |
| GSO | $5,752,000 | 32 | $3,629,000 | $2,094,000 | $0 | $29,000 | $0 |
| GSP | $1,162,000 | 77 | $398,000 | $759,000 | $0 | $5,000 | $0 |
| HNL | $167,000 | 106 | $26,000 | $141,000 | $0 | $0 | $0 |
| HOU | $12,179,000 | 12 | $11,207,000 | $598,000 | $0 | $374,000 | $0 |
| HPN | $5,283,000 | 35 | $1,976,000 | $2,514,000 | $0 | $793,000 | $0 |
| HSV | $564,000 | 89 | $382,000 | $165,000 | $0 | $17,000 | $0 |
| IAD | $9,718,000 | 17 | $5,095,000 | $4,584,000 | $0 | $39,000 | $0 |
| IAH | $14,353,000 | 9 | $11,532,000 | $2,811,000 | $0 | $10,000 | $0 |
| ICT | $1,102,000 | 79 | $661,000 | $406,000 | $0 | $35,000 | $0 |
| ILN | $0 | 120 | $0 | $0 | $0 | $0 | $0 |
| IND | $2,392,000 | 62 | $1,724,000 | $650,000 | $0 | $18,000 | $0 |
| ISP | $5,417,000 | 34 | $3,133,000 | $2,256,000 | $0 | $28,000 | $0 |
| JAN | $395,000 | 99 | $268,000 | $123,000 | $0 | $4,000 | $0 |
| JAX | $2,160,000 | 65 | $1,764,000 | $386,000 | $0 | $10,000 | $0 |
| JFK | $5,250,000 | 36 | $3,990,000 | $1,256,000 | $0 | $4,000 | $0 |
| JNU | $357,000 | 101 | $329,000 | $0 | $0 | $3,000 | $25,000 |
| LAS | $42,000 | 115 | $42,000 | $0 | $0 | $0 | $0 |
| LAX | $8,693,000 | 18 | $6,989,000 | $1,697,000 | $0 | $7,000 | $0 |
| LCK | $0 | 121 | $0 | $0 | $0 | $0 | $0 |
| LGA | $18,318,000 | 6 | $13,748,000 | $4,552,000 | $0 | $18,000 | $0 |
| LGB | $2,231,000 | 64 | $1,995,000 | $106,000 | $0 | $130,000 | $0 |
| LIT | $644,000 | 88 | $449,000 | $177,000 | $0 | $18,000 | $0 |
| MCI | $5,096,000 | 38 | $3,931,000 | $1,161,000 | $0 | $4,000 | $0 |
| MCO | $4,147,000 | 44 | $3,182,000 | $961,000 | $0 | $4,000 | $0 |
| MDT | $1,665,000 | 69 | $921,000 | $723,000 | $0 | $21,000 | $0 |
| MDW | $22,040,000 | 3 | $19,439,000 | $2,584,000 | $0 | $17,000 | $0 |
| MEM | $5,490,000 | 33 | $3,614,000 | $1,859,000 | $0 | $17,000 | $0 |
| MHT | $7,505,000 | 21 | $5,934,000 | $1,556,000 | $0 | $15,000 | $0 |
| MIA | $3,678,000 | 51 | $2,909,000 | $763,000 | $0 | $6,000 | $0 |
| MKE | $6,731,000 | 24 | $2,117,000 | $4,594,000 | $0 | $20,000 | $0 |
| MMU | $57,000 | 114 | $0 | $0 | $0 | $57,000 | $0 |
| MSP | $7,927,000 | 19 | $6,506,000 | $1,419,000 | $0 | $2,000 | $0 |
| MSY | $3,652,000 | 52 | $3,402,000 | $240,000 | $0 | $10,000 | $0 |
| OAK | $1,165,000 | 76 | $1,148,000 | $10,000 | $0 | $7,000 | $0 |
| OKC | $2,662,000 | 61 | $2,103,000 | $537,000 | $0 | $22,000 | $0 |
| OMA | $1,222,000 | 75 | $918,000 | $293,000 | $0 | $11,000 | $0 |
| ONT | $398,000 | 98 | $380,000 | $18,000 | $0 | $0 | $0 |
| ORD | $30,997,000 | 1 | $25,665,000 | $5,321,000 | $0 | $11,000 | $0 |
| ORF | $6,120,000 | 29 | $4,019,000 | $2,054,000 | $0 | $47,000 | $0 |
| PBI | $898,000 | 82 | $706,000 | $161,000 | $0 | $31,000 | $0 |
| PDX | $3,855,000 | 46 | $2,748,000 | $1,095,000 | $0 | $12,000 | $0 |
| PHL | $7,399,000 | 22 | $5,695,000 | $1,681,000 | $0 | $23,000 | $0 |
| PHX | $4,442,000 | 41 | $4,207,000 | $222,000 | $0 | $13,000 | $0 |
| PIE | $183,000 | 105 | $140,000 | $0 | $0 | $43,000 | $0 |
| PIT | $10,901,000 | 16 | $7,462,000 | $3,427,000 | $0 | $12,000 | $0 |
| PVD | $6,084,000 | 30 | $4,266,000 | $1,767,000 | $0 | $51,000 | $0 |
| RDU | $5,246,000 | 37 | $2,661,000 | $2,564,000 | $0 | $21,000 | $0 |
| RFD | $70,000 | 113 | $0 | $32,000 | $0 | $38,000 | $0 |
| RIC | $3,839,000 | 47 | $2,380,000 | $1,439,000 | $0 | $20,000 | $0 |
| RNO | $733,000 | 86 | $677,000 | $51,000 | $0 | $5,000 | $0 |
| ROC | $1,235,000 | 74 | $619,000 | $605,000 | $0 | $11,000 | $0 |
| RSW | $7,756,000 | 20 | $6,590,000 | $1,061,000 | $0 | $105,000 | $0 |
| SAN | $851,000 | 85 | $739,000 | $110,000 | $0 | $2,000 | $0 |
| SAT | $2,331,000 | 63 | $2,260,000 | $37,000 | $0 | $34,000 | $0 |
| SDF | $387,000 | 100 | $286,000 | $99,000 | $0 | $2,000 | $0 |
| SEA | $11,705,000 | 14 | $8,367,000 | $3,335,000 | $0 | $3,000 | $0 |
| SFB | $152,000 | 108 | $0 | $132,000 | $0 | $20,000 | $0 |
| SFO | $2,908,000 | 60 | $2,586,000 | $318,000 | $0 | $4,000 | $0 |
| SHV | $438,000 | 96 | $74,000 | $359,000 | $0 | $5,000 | $0 |
| SJC | $6,390,000 | 28 | $6,250,000 | $88,000 | $0 | $52,000 | $0 |
| SLC | $4,695,000 | 40 | $3,667,000 | $1,016,000 | $0 | $12,000 | $0 |
| SMF | $3,651,000 | 53 | $3,299,000 | $344,000 | $0 | $8,000 | $0 |
| SNA | $4,700,000 | 39 | $4,384,000 | $157,000 | $0 | $159,000 | $0 |
| STL | $3,407,000 | 54 | $2,862,000 | $541,000 | $0 | $4,000 | $0 |
| SWF | $164,000 | 107 | $42,000 | $117,000 | $0 | $5,000 | $0 |
| SYR | $1,030,000 | 81 | $493,000 | $534,000 | $0 | $3,000 | $0 |
| TEB | $272,000 | 104 | $0 | $0 | $0 | $272,000 | $0 |
| TLH | $1,799,000 | 67 | $368,000 | $1,363,000 | $0 | $68,000 | $0 |
| TPA | $2,934,000 | 59 | $2,575,000 | $326,000 | $0 | $33,000 | $0 |
| TRI | $295,000 | 103 | $39,000 | $251,000 | $0 | $5,000 | $0 |
| TUL | $874,000 | 84 | $623,000 | $241,000 | $0 | $10,000 | $0 |
| TUS | $35,000 | 116 | $34,000 | $0 | $0 | $1,000 | $0 |
| TYS | $1,098,000 | 80 | $476,000 | $612,000 | $0 | $10,000 | $0 |
| VNY | $71,000 | 112 | $0 | $0 | $0 | $71,000 | $0 |
| Total | $542,146,000 |  | $395,958,000 | $141,826,000 | $0 | $4,152,000 | $210,000 |

## Appendix K:	Data Sources

### Air traffic data

- Growth rates: Terminal Area Forecast (TAF)

- Scheduled traffic:  Official Airline Guide (OAG) and Flight Schedule Data System (FSDS)

- Unscheduled IFR traffic:  Enhanced Traffic Management System (ETMS)

- VFR traffic:  FAA Operations Network (OPSNET) data

- Cargo traffic:  DOT TranStats Schedule T-3 data; Cargo airlines

### Weather data

- National Climatic Data Center (NCDC) surface weather observations

### Flight data

- Airline Service Quality Performance (ASQP) database

- Aviation System Performance Metrics (ASPM) database

### Airport data

- National Flight Data Center (NFDC)

- DOT/FAA U.S. Terminal Procedures

- FAA Airport Capacity Benchmark Report

- FAA Operational Evolution Plan (OEP)

- FAA Airport Capacity Enhancement reports (ACE Plans)

- FAA ASD-430 Airport capacity and configuration data

- FAA National Airspace System Capital Investment Plan Fiscal Years 2004 – 2008

- FAA Blueprint for NAS Modernization

### Safety data

- National Transportation Safety Board (NTSB) accident and incident investigation database

- National Airspace Incidents Monitoring System (NAIMS)

- NASA’s Aviation Safety Reporting System (ASRS)

## Appendix L:	List of Acronyms

ACE		Aviation Capacity Enhancement

ADS-B	Automatic Dependent Surveillance – Broadcast

AILS		Airborne Information for Lateral Spacing

AIP		Airport Improvement Program

ANP		Actual Navigation Performance

APO		Office of Aviation Policy and Plans

ASDE-X	Airport Surface Detection Equipment – neXt generation

ASPM		Aviation System Performance Metrics

ASQP		Airline Service Quality Program

ATC		Air Traffic Control

ATM		Air Traffic Management

CAASD	Center for Advanced Aviation System Development

CDTI		Cockpit Display of Traffic Information

CFIT		Controlled Flight Into Terrain

CNS		Communication Navigation Surveillance

CONOPS	Concept of Operations

CONUS	Continental United States

DH		Decision Height

DME		Distance Measuring Equipment

DOC		Direct Operating Cost

EGNOS	European Geostationary Navigation Overlay Service

ETMS		Enhanced Traffic Management System

EVS		Enhanced Vision System

FAA		Federal Aviation Administration

FMS		Flight Management System

GA		General Aviation

FSDS		Flight Schedule Data System

GAME		GPS Approach Minima Estimator

GAO		General Accounting Office

GBAS		Ground Based Augmentation System

GDP		Gross Domestic Product

GLS		GNSS Landing System

GNSS 		Global Navigation Satellite System

GPS		Global Positioning System

GPS-III	Next-generation GPS

GS		Glide Slope

HUD		Head-Up Display

ICAO		International Civil Aviation Organization

IFR		Instrument Flight Rules

ILS		Instrument Landing System

IMC		Instrument Meteorological Conditions

IRU		Inertial Reference Unit
JPALS		Joint Precision Approach Landing System

LAAS		Local Area Augmentation System

LGF		LAAS Ground Facility

LNAV		Lateral Navigation

LOC		Localizer

LPV		Lateral Precision with Vertical Guidance

MMR		Multi-Mode Receiver

MSAS		MTSAT Space Augmentation System

MSL		Mean Sea Level

MTSAT	Multi-functional Transport Satellite

MVMC	Marginal VMC

NAS		National Airspace System

NASA		National Aeronautics and Space Administration

NCDC		National Climatic Data Center

NDB		Non-Directional Beacon

NFDC		National Flight Data Center

NPA		Non-Precision Approach

NTSB		National Transportation Safety Board

OAG		Official Airline Guide

OEM		Original Equipment Manufacturer

OMB		Office of Management and Budget

O&M		Operations and Maintenance

PAR		Precision Approach Radar

PFC		Passenger Facility Charge

PRM		Precision Runway Monitor

PTS		Passenger Time Savings

PVT		Position, Velocity, Time

RAIM		Receiver Autonomous Integrity Monitoring

RNAV		Area Navigation

RNP		Required Navigation Performance

RPM		Revenue Passenger Mile

RTM		Revenue Ton Mile

RVR		Runway Visual Range

SARPS	Standards and Recommended Practices

SBAS		Space Based Augmentation System

SIDs		Standard Instrument Departure Procedures

SOIT		Satellite Operational Integration Team

SPSS		Statistical Package for the Social Sciences

STARs		Standard Terminal Arrival Route

TAWS		Terrain Awareness and Warning System

TERPS	Terminal Instrument Procedures

VDB		VHF Data Broadcast

VFR		Visual Flight Rules

VHF		Very High Frequency

VMC		Visual Meteorological Conditions

VOR		VHF Omni-directional Range

WAAS		Wide Area Augmentation System

WAAS-GLS	WAAS GNSS (Global Navigation Satellite System) Landing System

WAAS-LPV	WAAS procedures with vertical guidance

## Appendix M:	Runway Utilization Analysis

Background

The utilization of runways is a key driver of LAAS straight-in and complex approach benefits estimates in this study.  Since the required data (i.e., observations of runway utilization for all runways at all of the airports studied, for all user equipment categories, and in various weather conditions) is not readily available, a method was developed for estimating arrival runway utilization in IMC from basic data, including wind direction and speed and current patterns of runway usage.

Wind direction is a primary factor for determining when a runway can be used.  However, other factors, including Air Traffic’s preferred configuration in specific weather conditions, also play a role, particularly under conditions of low wind speed. The following description illustrates the method used to accommodate both the current runway usage patterns and the observed wind data to arrive at estimates of future runway utilization during IMC. Port Columbus International Airport in Ohio (CMH) serves as an example.

Methodology

The method used in this analysis estimates the percentage of time that a runway could be utilized based on wind direction and speed, and then modifies that percentage by taking into account the characteristics of each runway and a measure of preferred usage of runways, based on objective data.

Wind Speed and Direction

At wind speeds lower than a certain threshold, the airport configuration, and therefore the arrival runways in use, can be determined by the preferred configuration, and need not be dependent on wind direction.  Above this wind speed threshold, however, the wind direction is a key factor in determining which runways can be used.  Based on aircraft performance data and interviews with airline and airport operations staff, a wind speed threshold of 10 knots was selected.

The wind direction analysis uses historical weather data, including wind speed and direction, and current runway usage data in order to estimate the arrival runway utilization for each runway at each airport within the benefits study.  Historical weather data covering 1998 through 2001 has been collected for the 121 airports from the NCDC database. Wind direction has been tabulated for the percent of time that wind speeds greater than 10 knots occur in each cardinal direction in two weather conditions, Visual and IMC.  Table M1 shows an example of this data for CMH.

Table M1: Wind Direction at CMH (Wind Speed Greater Than 10 Knots, in Each Weather Condition)

| Airport | Weather | E | N | NE | NW | S | SE | SW | W | Less than 10 knots |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CMH | IMC | 0.92% | 3.18% | 0.96% | 2.96% | 1.96% | 0.88% | 2.72% | 3.44% | 82.98% |
|  | Visual | 0.71% | 1.45% | 0.87% | 3.43% | 2.16% | 0.59% | 4.46% | 6.29% | 80.04% |

To calculate the wind-direction-based availability of a runway the percent of time that winds greater than 10 knots are in this direction are added to the percent of time that winds are less than 10 knots divided among the possible arrival runways.  Using the percentages in Table M1, an eastbound runway would be available 82.98% of the time divided by the number of possible runways, plus 0.92% of the time that winds are greater than 10 knots for this direction. The following formula shows how the availability of an eastbound runway at CMH is calculated. Note that two arrival runways are assumed for this example (as will be shown in the following section).

Eastbound Runway Availability = 82.98% ( 2 + 0.92% = 42%

Runway Characteristics and Preferred Usage

Current runway configurations have been gathered from several sources, including FAA’s ASD organization and the FAA’s airport-specific capacity enhancement plans. Table M2 shows the runways identified as arrival runways in any weather condition for CMH.

Table M2: Runways Used for Arrivals at CMH

| Airport | Runway | Listed As An Arrival Runway? | Source |
| --- | --- | --- | --- |
| CMH | 10L | Yes | ASD; ACE Plan |
| CMH | 10R | Yes | ASD; ACE Plan |
| CMH | 28R | Yes | ASD; ACE Plan |
| CMH | 28L | Yes | ASD; ACE Plan |

Runway length is an important consideration in this analysis. A runway is only available for arrivals for a particular equipment category (e.g., large jet) if it meets the length requirement for that type of equipment.  Runway length requirements were established by searching various databases containing aircraft performance characteristics, and specific aircraft types were selected as representative for the entire aircraft population. Table M3 lists the runway length requirements applicable for each equipment category included in this study. Table M4 lists the arrival runway lengths at CMH, showing that all runways in consideration are of sufficient length to accommodate any equipment type.

Table M3: Runway Length Requirements for Each Equipment Category

| Equipment Category | Example Aircraft | Runway Length Requirement (ft) |
| --- | --- | --- |
| Heavy Eqpt | D10; B757 | 6250 |
| Large Jet Eqpt | B737; M80 | 6250 |
| Large Commuter | CRJ | 5750 |
| Small Commuter | BE1 | 3750 |
| Small Eqpt | CNA; PAG (typically Alaska-based regional carriers) | 2750 |

Table M4: Runway Lengths at CMH

| Airport | Runway | Runway Length (ft) |
| --- | --- | --- |
| CMH | 10L | 8000 |
|  | 10R | 10250 |
|  | 28R | 8000 |
|  | 28L | 10250 |

If any runway at CMH were shorter than the requirement for a particular category, that runway would be dropped from consideration for that equipment type.  Thus, at any airport, a particular runway may be available for utilization by some or all equipment categories.

Additionally, multiple parallel runways may not be available for simultaneous independent arrivals in IMC if their centerline separation is less than 4300 feet.  In these circumstances the runway to retain is selected based on the following sequence of rules: Retain the runway with the most capable landing system (e.g., ILS Cat III vs. ILS Cat I), or the lowest approach minima (decision height and visibility), or the longest runway.  The other parallel runway will be dropped from consideration. This provides an objective way to retain those runways most likely to be used for arrivals in IMC, and provides a level of conservatism to the results, since in some cases, these parallel runways might actually be used for dependent parallel approach operations. Table M5 illustrates how two of the runways at CMH (10L and 28R) were dropped from consideration due to close parallel separation distances.  In this case, the only objective distinction between these runways is the length, which leads to 10L and 28R being omitted from further consideration.

Table M5: Parallel Runway Analysis Details for CMH

| Airport | Runway ID | Separation Between Parallel Runways (ft) | Best Approach Minima | Best Landing System | Runway Length (ft) | Runway to Drop |
| --- | --- | --- | --- | --- | --- | --- |
| CMH | 10L | 2804 | 200/2400 | ILS Cat I | 8000 | 10L |
|  | 10R |  | 200/2400 | ILS Cat I | 10250 |  |
|  | 28R | 2804 | 200/2400 | ILS Cat I | 8000 | 28R |
|  | 28L |  | 200/2400 | ILS Cat I | 10250 |  |

It is understood that airport operators and Air Traffic will have a preference for using certain runways over others, depending on weather conditions. To account for this preference, the practice established in the FAA’s “Airway Planning Standard Number One - Terminal Air Navigation Facilities and Air Traffic Control Services” document was followed. That is, the arrival runway most likely to be preferred was designated as the “Primary” runway, and other arrival runways were designated as “Secondary”.  Specifically, the runway with the lowest approach minima was designated as “Primary”.  In recognition that the majority of traffic is directed to the most capable runway, a weighting of 70%  is applied to the primary runway and the remaining 30% is shared among the secondary runways. In cases where there are only Primary runways (i.e., no distinctions between runway capabilities), a 50/50 weighting is applied. This weighting is applied to the percentage of time the wind speed is less than 10 knots, when runway configuration preferences, rather than wind direction, is a primary decision factor. Table M6 illustrates how these weighting factors were applied to the two remaining arrival runways at CMH (both considered primary since they have the same type of ILS, identical approach minima, and runway length).

Table M6: Runway Weighting Factor Details for CMH

| Airport | Runway | Runway Length | Arrival Runway ? | Utilization Based on Wind Direction | Best Landing System | Approach Minima | Primary or Secondary Runway ? | Runway Weighting Factor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CMH | 10L | 8000 | No; Dropped due to parallel spacing | N/A | ILS Cat I | 200/ 2400 | N/A | N/A |
| CMH | 10R | 10250 | Yes | 0.42 | ILS Cat I | 200/ 2400 | Primary | 0.5 |
| CMH | 28R | 8000 | No; Dropped due to parallel spacing | N/A | ILS Cat I | 200/ 2400 | N/A | N/A |
| CMH | 28L | 10250 | Yes | 0.46 | ILS Cat I | 200/ 2400 | Primary | 0.5 |

Results

Table M7 summarizes the results of this arrival runway utilization analysis for CMH.  As shown in Table M5, runways 10L and 28R drop out due to parallel separation requirements. The wind direction analysis, Table M1, showed that approximately 42% of the time winds were either lower than 10 knots or were aligned with 10R, and 46% of the time with 28L.  Since both runways have nearly identical landing systems and approach minima, both are designated “Primary” runways in Table M6, and a 50/50 weighting is applied to arrive at the final runway utilization of 47% [=(0.92+(82.98/2)*.5)/((0.92+(82.98/2)*.5)+(3.44+(82.98/2)*.5))] for 10R and 53% for 28L.

Table M7: Summary of Estimated Arrival Utilization by Runway at CMH

| Airport | Runway | Primary Wind Direction | Runway Length | Currently Used As An Arrival Runway ? | Considered as an IMC Arrival Runway for this Study ? | Utilization Based on Wind Direction | Primary or Secondary Runway ? | Runway Weighting Factor | Heavy Equipment Weighted Utilization in IMC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CMH | 10L | East | 8000 | Yes | No |  |  |  | 0% |
| CMH | 10R | East | 10250 | Yes | Yes | 42% | Primary | 0.5 | 47% |
| CMH | 28R | West | 8000 | Yes | No |  |  |  | 0% |
| CMH | 28L | West | 10250 | Yes | Yes | 46% | Primary | 0.5 | 53% |

For validation of this result, the utilizations above can be compared to the individual capacity enhancement plan for CMH.  This report shows that in IMC, there is a 45% utilization for east flow (runways 10L/R), and 55% for west flow (runways 28L/R).

Appendix N:	Analysis of the Downstream Effect of Delays

Background

Flight disruptions of the kind studied here are not isolated events.  In general, a single flight disruption may have an impact on a number of other flight operations.  This connection between disruptions can be accounted for either by formally modeling the network effects that link flight operations, or by adding a factor for “downstream” effects.  Network effects include the impact of a reduced rate of operations at one airport on operations at other airports, and the recognition that a weather-related disruption at one airport, particularly an airline’s hub, can have substantial detrimental effects throughout that airline’s network.  In this report, downstream effects of a flight disruption are accounted for through a factor that is multiplied by the initial disruption. A network model of the NAS is employed to establish support for selecting the correct downstream effect multiplier. Additionally, due to the importance of this factor, and the uncertainty surrounding its proper value, the downstream factor is also included in the sensitivity analysis.

Methodology

The specific value chosen for this factor has a substantial impact on total benefits. The estimate used in this study is based on published research  and prior FAA usage of downstream effects of delays, the single most common form of disruption. It is recognized that such downstream factors for delays vary significantly with both the magnitude of the original delay and the time of day at which it occurs, with reported factors ranging from 1.0 to 13.  Earlier studies have been conducted using observed flight data covering a limited number of flights. In this study, these observation-based results were extended to a larger fraction of all NAS flights by applying a simulation model.  For this effort, the National Airspace System Performance Analysis Capability (NASPAC) simulation model was employed.  NASPAC simulates all air traffic over the NAS including commercial, general aviation, and military flights, with a detailed simulation covering 80 airports.  Among its inputs are flight schedules, flight path data, ground holds, and changes in airport capacity due to weather or other factors.  Outputs of NASPAC include many detailed delay data files which allow tracking of delay by aircraft. It should be noted that this analysis only looked at the ripple delay associated with a single aircraft.  Thus, this result may be conservative since it does not include the impact that the delayed aircraft has on other flights.  For example, delayed arrival of passengers, baggage, equipment, and crews can cause delay in other flights within a carrier’s network.

Three NASPAC simulations were performed for varying weather conditions, based on actual weather observations for three days.  These three days were chosen for their range of weather-related delays reported by the FAA’s OPSNET database and included a good weather day, with relatively few weather-related delays, an average day, and a poor weather day.  This range of input values allows the exploration of a wider variety of NAS performance conditions, including a range of initial delays, than would be possible by analyzing a single “typical” day.

Arrival delay outputs of the simulation model were then analyzed.  In order to remain consistent with the calculation of downstream effect from previous studies, the following formula was used:

where DF is the downstream factor, Di is the initial delay and Dd is the sum of subsequent delays.

In analyzing the data, individual aircraft were followed throughout the day by tracking their tail numbers in NASPAC output files.  Only flights that incurred initial delays greater than 15 minutes were included in the analysis.  In calculating the downstream effect for a specific aircraft, the initial delay used in the calculation, Di, was the number of minutes of delay in the first delayed flight segment for that particular aircraft.  The downstream delay used was the sum of the number of minutes of delay for all flight segments of that same aircraft after the initial delay flight segment.  Using this method, a DF for every delayed aircraft was calculated.  For example, a particular aircraft simulated in NASPAC which started the day with a flight from OAK to BUR was delayed 53 minutes.  These 53 minutes are the initial delay (Di) for this aircraft.  The same plane subsequently was simulated to have flown to LAS where it was 36 minutes delayed, and then to SAT where it was 31 minutes delayed, and finally to MIA where it was on-time.  Summing the subsequent delays (Dd) after the initial delay, we find that this aircraft experienced 67 (=  36 + 31 + 0) minutes of delay.  Using the formula for downstream factor, we find that DF = (53 + 67) / 53 = 2.3.  Therefore the downstream delay effect calculated for this aircraft’s simulated day was 2.3.

Thus, for each delayed aircraft, values were obtained for the magnitude of initial delay, the time of day of initial delay, and the downstream effect factor associated with that initial delay. These results were tabulated, following the example of Beatty et al , by magnitude of initial delay and time of day. Additionally, descriptive statistics were evaluated from the overall results, including mean and median DF.

Results

Previous studies have shown that the magnitude of the DF is strongly dependent on both increased magnitude of initial delay and time of day of the initial delay (larger factor for initial delays that occur earlier in the day).  The results of this analysis were consistent with those findings.  However, differences in DF among the three simulated days were minimal, as increases in the number and duration of initial delays due to the addition of bad weather to the simulation were offset by similar increases in downstream delays, resulting in a similar overall range of DF ratios for each simulated day.  Thus, in order to work with the richest data, the simulated day with the largest number of delays (that is, the simulated day with the poorest weather) was selected for further analysis.  Table N1 reports DF by size of initial delay and the time of day that the initial delay was incurred.  Columns in Table N1 represent initial delay groups of 15 to 24 minutes, 25 to 34 minutes, and so forth.

Table N1. Downstream Factor by Initial Delay and Time of Day

(Blank entries indicate cells with insufficient observed delays)

|  | INITIAL DELAY (Minutes) |
| --- | --- |
| TIME | 15 | 25 | 35 | 45 | 55 | 65 | 75 | 85 | 95 | 105 | 115 | 125 | 135+ |
| 6:00 | 5.1 |  |  |  |  |  |  |  |  |  |  |  |  |
| 7:00 | 9.7 | 6.1 | 10.6 |  |  |  |  |  |  |  |  |  |  |
| 8:00 | 6.3 | 6.3 | 7.0 | 6.6 | 12.8 | 12.8 |  |  |  |  |  |  |  |
| 9:00 | 4.5 | 5.0 | 4.0 | 5.5 | 6.1 | 7.7 |  |  |  |  |  |  |  |
| 10:00 | 4.4 | 3.7 | 5.3 | 6.9 | 5.0 | 3.3 |  | 4.7 |  | 4.1 | 8.1 |  |  |
| 11:00 | 3.7 | 3.2 | 3.8 | 3.5 | 4.7 | 5.4 | 2.7 | 3.9 | 5.5 | 8.3 | 6.6 |  |  |
| 12:00 | 3.2 | 2.8 | 3.1 | 3.2 | 4.8 | 5.5 | 5.8 | 3.0 | 2.6 | 2.7 |  |  | 6.6 |
| 13:00 | 2.7 | 3.1 | 4.4 | 3.3 | 3.8 | 3.1 | 3.4 | 4.3 |  | 5.1 |  |  | 5.1 |
| 14:00 | 2.5 | 2.5 | 2.5 | 3.7 | 4.4 | 3.6 | 3.1 | 4.1 | 5.0 | 1.9 | 2.5 | 3.7 | 4.5 |
| 15:00 | 3.0 | 2.7 | 3.0 | 3.5 | 2.6 | 3.3 | 4.3 | 2.9 | 2.9 | 3.2 | 3.8 | 2.9 | 5.1 |
| 16:00 | 2.5 | 2.4 | 2.6 | 3.0 | 2.9 | 2.5 | 3.4 | 3.7 | 3.1 | 2.9 | 3.0 | 3.6 | 5.2 |
| 17:00 | 2.1 | 2.2 | 2.2 | 2.6 | 1.9 | 3.4 | 3.2 | 3.8 | 2.3 | 2.3 |  | 3.9 | 4.2 |
| 18:00 | 1.7 | 1.5 | 1.7 | 2.0 | 2.6 | 2.4 | 2.0 | 3.2 | 2.4 | 3.5 | 2.2 | 3.5 | 3.4 |
| 19:00 | 1.7 | 1.5 | 1.8 | 1.6 | 1.7 | 1.9 | 2.4 | 1.8 | 3.1 | 2.5 | 4.3 | 2.0 | 2.5 |
| 20:00 | 1.3 | 1.3 | 1.4 | 1.5 | 1.4 | 1.6 | 1.4 | 1.4 | 2.1 | 2.1 | 1.9 | 1.7 | 2.6 |
| 21:00 | 1.3 | 1.1 | 1.1 | 1.4 | 1.5 | 1.2 | 1.1 | 1.3 | 1.5 | 1.8 | 1.7 | 2.5 | 2.2 |
| 22:00 | 1.0 | 1.0 | 1.2 | 1.2 | 1.2 | 1.3 | 1.4 | 1.0 | 1.6 | 1.7 | 1.3 | 1.9 | 1.5 |
| 23:00 | 1.1 | 1.1 | 1.0 | 1.1 | 1.0 | 1.1 | 1.1 | 1.0 |  | 1.5 | 1.2 | 1.9 | 1.5 |
| 0:00 | 1.0 | 1.0 | 1.0 | 1.0 | 1.1 | 1.0 | 1.0 |  | 1.0 | 1.0 | 1.0 | 1.0 | 1.1 |
| 1:00 | 1.0 | 1.1 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 |  |  | 1.0 | 1.0 | 1.0 | 1.0 |
| 2:00 | 1.0 | 1.0 |  |  |  |  |  |  |  |  |  |  | 1.0 |
| 3:00 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4:00 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5:00 |  |  |  |  |  |  |  |  |  |  |  |  |  |

In order to determine an appropriate single value of the DF to use in the efficiency benefits analyses, a weighted mean DF was calculated that accounted for the time distribution of delayed air traffic arrivals, and the magnitude of initial delays.  Figure N1 shows the mean DF for each hour of the day, and the timing of delayed air traffic arrivals reported in the simulation outputs.

Figure N1. Downstream Factor and Delayed Arrivals by Time

Finally, the mean DF for each hour was multiplied by the percentage of delayed arrival traffic occurring during that hour for each delay group.  By using a traffic-weighted mean, a more realistic representation of the true downstream effect of delays is achieved, and one that is applicable to all delays, regardless of their time of occurrence. Mathematically, this is shown as follows:

where DFw is the weighted downstream factor, DFtx is the mean downstream factor at time t in initial delay group x, Atx is the arrival traffic at time t in delay group x, and A is the sum of all delayed arrival traffic.  Note that the arrival traffic accounts only for the number of delayed flights, not overall traffic.  The resulting weighted mean DF is 2.6.

Similarly, a weighted mean DF was calculated for use only with takeoff disruptions, based on the time distribution of low visibility conditions relevant to these disruptions.  The resulting weighted mean DF for takeoff disruptions is 3.7.

Summary

This study provides support to previous findings that a wide range of downstream factors is possible, depending on the timing and magnitude of the initial delay.  Although this study showed that 2.6 is a reasonable single value for this factor, given the poor weather included in the simulation, previous similar studies have used lower values. Thus, an intermediate value of 1.8 was chosen as the primary DF for use in the LAAS Benefits Analysis.

Appendix O:	Severe Weather Categories Eliminated From This Analsyis

Table O1: NCDC Indicators Used to Eliminate Severe Weather

Appendix P: 	Cargo ‘Box Value of Time’ by Airport

Table P1: Discounted 20 year LAAS Benefits – Box Value of Time for Cargo-only Operators, by Airport

| Airport | Box Value of Time LAAS Benefit |
| --- | --- |
|  | 0% waas equipage scenario | 100% waas equipage scenario |
| ABQ | $1,270,000 | $723,000 |
| ACK | $1,249,000 | $1,249,000 |
| AFW | $885,000 | $885,000 |
| ALB | $4,089,000 | $2,906,000 |
| ANC | $19,514,000 | $11,337,000 |
| ATL | $1,795,000 | $1,489,000 |
| AUS | $0 | $0 |
| AVL | $12,000 | $12,000 |
| BDL | $5,676,000 | $2,024,000 |
| BFI | $1,341,000 | $1,341,000 |
| BGR | $211,000 | $211,000 |
| BHM | $1,865,000 | $0 |
| BNA | $536,000 | $136,000 |
| BOI | $1,109,000 | $1,109,000 |
| BOS | $1,561,000 | $1,561,000 |
| BUF | $1,360,000 | $1,155,000 |
| BUR | $2,558,000 | $196,000 |
| BWI | $1,056,000 | $1,056,000 |
| CAE | $2,538,000 | $1,564,000 |
| CHA | $187,000 | $187,000 |
| CHS | $457,000 | $241,000 |
| CLE | $5,564,000 | $1,208,000 |
| CLT | $1,659,000 | $1,659,000 |
| CMH | $7,000 | $7,000 |
| COS | $2,028,000 | $1,787,000 |
| CVG | $6,235,000 | $4,274,000 |
| DAB | $0 | $0 |
| DAL | $509,000 | $509,000 |
| DAY | $3,697,000 | $1,941,000 |
| DCA | $0 | $0 |
| DEN | $2,588,000 | $2,588,000 |
| DFW | $8,825,000 | $4,218,000 |
| DLH | $149,000 | $149,000 |
| DSM | $1,362,000 | $1,362,000 |
| DTW | $3,116,000 | $1,468,000 |
| DVT | $0 | $0 |
| ELP | $47,000 | $47,000 |
| EUG | $3,663,000 | $3,344,000 |
| EWR | $4,418,000 | $4,418,000 |
| EYW | $0 | $0 |
| FAI | $204,000 | $204,000 |
| FAT | $197,000 | $197,000 |
| FLL | $664,000 | $664,000 |
| FWA | $5,253,000 | $1,256,000 |
| FXE | $0 | $0 |
| GEG | $6,840,000 | $4,004,000 |
| GRR | $4,952,000 | $4,122,000 |
| GSO | $3,435,000 | $3,435,000 |
| GSP | $322,000 | $322,000 |
| HNL | $1,125,000 | $0 |
| HOU | $8,000 | $8,000 |
| HPN | $5,000 | $5,000 |
| HSV | $880,000 | $880,000 |
| IAD | $809,000 | $809,000 |
| IAH | $1,086,000 | $1,086,000 |
| ICT | $1,696,000 | $865,000 |
| ILN | $6,656,000 | $6,656,000 |
| IND | $6,341,000 | $6,341,000 |
| ISP | $0 | $0 |
| JAN | $200,000 | $200,000 |
| JAX | $738,000 | $738,000 |
| JFK | $2,414,000 | $2,414,000 |
| JNU | $15,763,000 | $512,000 |
| LAS | $0 | $0 |
| LAX | $1,528,000 | $1,528,000 |
| LCK | $936,000 | $936,000 |
| LGA | $0 | $0 |
| LGB | $5,922,000 | $4,708,000 |
| LIT | $171,000 | $171,000 |
| MCI | $1,335,000 | $1,335,000 |
| MCO | $1,882,000 | $1,040,000 |
| MDT | $1,861,000 | $1,861,000 |
| MDW | $153,000 | $153,000 |
| MEM | $16,222,000 | $15,191,000 |
| MHT | $6,032,000 | $4,946,000 |
| MIA | $3,459,000 | $2,037,000 |
| MKE | $8,388,000 | $3,401,000 |
| MMU | $0 | $0 |
| MSP | $642,000 | $642,000 |
| MSY | $1,755,000 | $648,000 |
| OAK | $1,980,000 | $1,471,000 |
| OKC | $2,092,000 | $1,076,000 |
| OMA | $1,028,000 | $1,028,000 |
| ONT | $346,000 | $346,000 |
| ORD | $3,063,000 | $3,063,000 |
| ORF | $2,293,000 | $2,270,000 |
| PBI | $259,000 | $43,000 |
| PDX | $1,555,000 | $1,555,000 |
| PHL | $2,256,000 | $2,256,000 |
| PHX | $1,121,000 | $1,121,000 |
| PIE | $519,000 | $411,000 |
| PIT | $1,130,000 | $1,130,000 |
| PVD | $1,987,000 | $1,694,000 |
| RDU | $803,000 | $803,000 |
| RFD | $8,645,000 | $4,780,000 |
| RIC | $3,483,000 | $2,024,000 |
| RNO | $948,000 | $214,000 |
| ROC | $1,697,000 | $833,000 |
| RSW | $843,000 | $843,000 |
| SAN | $2,631,000 | $119,000 |
| SAT | $1,006,000 | $1,006,000 |
| SDF | $1,694,000 | $1,694,000 |
| SEA | $3,226,000 | $2,997,000 |
| SFB | $0 | $0 |
| SFO | $204,000 | $204,000 |
| SHV | $547,000 | $263,000 |
| SJC | $2,609,000 | $1,622,000 |
| SLC | $1,651,000 | $1,651,000 |
| SMF | $1,589,000 | $1,589,000 |
| SNA | $557,000 | $557,000 |
| STL | $9,000 | $9,000 |
| SWF | $129,000 | $21,000 |
| SYR | $692,000 | $379,000 |
| TEB | $409,000 | $93,000 |
| TLH | $1,725,000 | $1,725,000 |
| TPA | $368,000 | $368,000 |
| TRI | $59,000 | $59,000 |
| TUL | $244,000 | $136,000 |
| TUS | $5,000 | $5,000 |
| TYS | $672,000 | $672,000 |
| VNY | $0 | $0 |
| Total | $259,084,000 | $173,806,000 |

Appendix Q:	Government and Industry Contributors

The IBM team wishes to recognize the following organizations and individuals for providing feedback on the LAAS benefits analysis work.  Appearance on this list is an indication that each individual was afforded an opportunity to comment on IBM’s benefits analysis approach; it does not imply agreement with IBM’s approach.

An asterisk (*) denotes a primary Point of Contact for each organization.

### Airport and Airline Site Visits

A critical element of this study was the involvement of representatives from the aviation industry, including airlines, airports, air traffic service providers, and equipment manufacturers.  The following individuals provided subject matter expertise, data and valuable feedback:

Table P1: Airport and Airline Site Visits

| Visit Date | Organization | Contact | Position |
| --- | --- | --- | --- |
| 02-Feb-2004 | Federal Express | Cole, Ray | Aircraft Standards Engineer |
| 02-Feb-2004 | Federal Express | Murdoch, Joel | *Manager, Strategic Projects |
| 02-Feb-2004 | Federal Express | Vail, Steve | Senior Manager of Global Air Traffic |
| 03-Feb-2004 | Shelby County Airport Authority | White, Walter | *Director of Operations and Public Safety |
| 03-Feb-2004 | FAA | Wertz, Bill | *MEM ATCT Manager |
| 05-May-2004 | Boeing | Ackland, John | *Senior Technical Fellow – Airplane Systems |
| 05-May-2004 | Boeing | Alcabin, Monica | Principal Engineer |
| 05-May-2004 | Boeing | Malsom, Don | Associate Director Business Development – Air Traffic Management |
| 05-May-2004 | Boeing | Michael, Bob | Product Manager Marketing & Business Strategy |
| 05-May-2004 | Boeing | Siegmund, Paul | Program Manager, Regulatory Affairs |
| 05-May-2004 | Boeing | Sipe, Alan | -- |
| 05-May-2004 | Boeing | Tuttle, Tim | Program Manager, Product Development |
| 05-May-2004 | FAA | Beckerdite, Ron | *SEA TRACON Facility Manager |
| 05-May-2004 | Seattle Tacoma Airport | Kikillus, Rob | *SEA Operations Development Manager, Airfield |
| 05-May-2004 | FAA | Vernon, Kathryn | *SEA ATCT Facility Manager |
| 06-May-2004 | Alaska Airlines | Dalton, Sarah | * Director of Flight Operations |
| 06-May-2004 | Horizon Airlines | Solmonson, Perry | *Manager Flight Operations Technical |
| 17-May-2004 | BDL | Tebbetts, Roland | BDL Ops Manager |
| 17-May-2004 | FAA | Bellabona, Joseph | Regional SR Ops Research Spc/ANE 520.6 |
| 17-May-2004 | FAA | Fiske, Gary | *BDL Tower/TRACON |
| 17-May-2004 | FAA | Guiod, Mark | BDL Air Traffic Manager |
| 17-May-2004 | FAA | Hall, David L | Flight Standards – NE Region |
| 19-May-2004 | FAA | Gross, Stu | EWR ATC |
| 19-May-2004 | FAA | Jennings, Al | EWR ATC Manager |
| 19-May-2004 | FAA | Sandes, Larry | EWR ATC |
| 19-May-2004 | FAA | Wagner, Mike | *EWR ATC |
| 20-May-2004 | FAA | Kalpaxis, Timon | NATCA N90 |
| 20-May-2004 | FAA | Moss, Patti | *N90 Airspace |
| 20-May-2004 | NY,NJ Port Authority | Gatto, Ralph | *Senior Airport Engineer |
| 03-Jun-2004 | City of Chicago, Dept of Aviation | Foggia, John | Consultant |
| 03-Jun-2004 | City of Chicago, Dept of Aviation | Santos, Joe | *Executive Assistant |
| 03-Jun-2004 | City of Chicago, Dept of Aviation | Bierbrodt, Jeffery | Consultant |
| 08-Jun-2004 | United Airlines | Baas, Jim | Manager, Capacity Enhancement |
| 08-Jun-2004 | United Airlines | Burns, Joe | Director, Flight Standards and Technology |
| 08-Jun-2004 | United Airlines | Haynes, Brian | Manager, Flight Operations Technology |
| 08-Jun-2004 | United Airlines | Holford, Tom | Manager, Navigation Upgrades |
| 08-Jun-2004 | United Airlines | Stone, Rocky | *Manager, Flight Systems Technology |
| 08-Jun-2004 | ATNSI | Murphy, Mike | *Consultant |
| 17-Jun-2004 | Continental Airlines | Vaughn, Bill | *Manager Advanced Navigation |
| 21-Jun-2004 | Southwest Airlines | Crum, Greg | Vice President Flight Operations and Chief Pilot |
| 21-Jun-2004 | Southwest Airlines | Edens, Dave | Chief Pilot |
| 21-Jun-2004 | Southwest Airlines | Gleason, Brian | * Director, Flight Operations Technical |
| 21-Jun-2004 | Southwest Airlines | Haynes, Rob | Regional Chief Pilot |
| 21-Jun-2004 | Southwest Airlines | Humphrey, Stan D. | Pilot |
| 21-Jun-2004 | Southwest Airlines | Johns, Frank | Air Traffic Coordinator |
| 21-Jun-2004 | Southwest Airlines | Mullis, Phil | Air Traffic Coordinator |
| 21-Jun-2004 | Southwest Airlines | Stephens, Jon | Senior Financial Planning Analyst |
| 21-Jun-2004 | Southwest Airlines | Ward, Edward T. | Manager, Navigation Data |
| 21-Jun-2004 | Southwest Airlines | Wiecek, Kevin | Flight Operations Engineer |

### Federal Aviation Administration (FAA)

The following individuals from the FAA provided subject matter expertise, data and feedback:

Table P2: FAA Contributors

| Organization | Contact | Position |
| --- | --- | --- |
| FAA, AFS-430 | Jarvis, Ed | Flight Standards |
| FAA, AIR-130 | Abduselam, Hamza | Certification |
| FAA, AIR-130 | DeCleene, Bruce | Certification |
| FAA, AOP-200/ATO-W | Tran, Deborah | NASPAS Program |
| FAA, ARN-100 | Williams, Ammyanna |  |
| FAA, ATO-R | MacNeill, Ken | AT Requirements |
| FAA, ATO-W | Peterson, Dave | OIT Team Lead |
| FAA, ATO-P | Citrenbaum, Dan | Operations Research Division |
| FAA, ATO-PFAA, ASD-420 | Wright, Wes | Business Case Analysis Division |
| FAA, ATO-PFAA, ASD-420 | Depasquantonio, Maria | Manager, Business Case Analysis Division |
| FAA, ATO-PFAA, ASD-430 | Melone, Fran | Manager, Operations Research Division |
| FAA, ATO-PFAA, ASD-430 | Coleman, Nastaran | Operations Research Division |
| FAA, ATO-W | Bell, Hal | WAAS PT Lead |
| FAA, ATO-W/AMTI | Noto, John | WAAS Task Lead |
| FAA, ATO-W/ESC/ARINC | Packard, Richard | JPALS Liaison |
| FAA, ATO-W/ISI | Lay, Richard | LAAS System Engineer |
| FAA, Navigation Services, ATO-W | Rixmann, Gary | (former MLS Contract Technical Officer) Lighting Systems Office |

### MITRE/CAASD

The following individuals from MITRE/CAASD, listed in alphabetical order by last name, provided subject matter expertise, tools, data and valuable feedback:

Table P3: MITRE/CAASD Subject Matter Experts

| Organization | Contact | Position |
| --- | --- | --- |
| MITRE/CAASD | Barrer, John | Lead Engineer |
| MITRE/CAASD | Markin, Kelly | Program Manager |
| MITRE/CAASD | Massimini, Vince | Senior Principal Engineer |
| MITRE/CAASD | Scales, Walt | Project Team Manager |
| MITRE/CAASD | Swedish, William | Principal Engineer |

### Conference Calls with Major Airline Representatives

The following individuals, listed in alphabetical order by organization, participated in discussions of the LAAS Benefits Analysis:

Table P4: LAAS Benefits Discussion Airline Representative Participants

| Organization | Contact | Position |
| --- | --- | --- |
| Alaska Airlines | Dalton, Sarah | Director of Flight Operations |
| American Trans Air | Enias, James | Technical Pilot |
| Boeing | Ackland, John | Senior Technical Fellow Airline System |
| Continental Airlines | Vaughn, Bill | Captain, Flight Technical |
| Delta Airlines | Speir, Ken | Fleet Technical Pilot |
| Federal Express | Murdock, Joel | Manager, Strategic Projects |
| Honeywell | Hoodspith, Mike | Manager, Satellite Landing Systems, Commercial Products, Asia, Latin America & Western U.S. |
| Horizon Airlines | Bush, Steve | Flight Ops Technical |
| JetBlue Airways | Somerville, Donald | Captain, GPS/RNAV Subject Matter Specialist |
| Northwest Airlines | Alexander, Frank | Chief Pilot Technical Programs |
| Southwest Airlines | Gleason, Brian | Director, Flight Operations Technical |
| United Airlines | Stone, Rocky | Manager of Flight Systems Technology |
| United Parcel Service | Hilb, Bob | Manager of Advanced Flight Systems |

### GBAS FAA-Europe Coordination Meeting, April 2004

The following meeting participants provided subject matter expertise, data and valuable feedback:

Table P5: GBAS FAA-Europe Subject Matter Experts

| Organization | Contact | Position |
| --- | --- | --- |
| EUROCONTROL | Grand-Perret, Sylvie | *Expert – Navigation |
| SKYGUIDE | Berz, Gerhard | *System Engineer, Satellite Navigation |
| SOFREAVIA | De La Burgade, Olivier | Consulting Division, Project Manager |

Appendix R:	Number of ILSs Required to Achieve Equivalent LAAS Benefit

Table R1: Number of ILSs Required to Achieve Equivalent LAAS Benefit

|  | 0% WAAS Equipage | 100% WAAS Equipage |
| --- | --- | --- |
| Airport | No. of Cat I ILS | No. of Cat I to Cat II/III Upgrades | No. of New Cat II/III ILS | No. of Cat I ILS | No. of Cat I to Cat II/III Upgrades | No. of New Cat II/III ILS |
| ABQ | 1 | 3 | 0 | 1 | 3 | 0 |
| ACK | 0 | 2 | 0 | 0 | 2 | 0 |
| AFW | 0 | 1 | 0 | 0 | 1 | 0 |
| ALB | 1 | 3 | 0 | 1 | 3 | 0 |
| ANC | 1 | 2 | 0 | 1 | 2 | 0 |
| ATL | 0 | 1 | 0 | 0 | 1 | 0 |
| AUS | 0 | 1 | 0 | 0 | 1 | 0 |
| AVL | 0 | 1 | 0 | 0 | 1 | 0 |
| BDL | 1 | 3 | 0 | 1 | 3 | 0 |
| BFI | 0 | 2 | 0 | 0 | 2 | 0 |
| BGR | 0 | 1 | 0 | 0 | 1 | 0 |
| BHM | 2 | 3 | 0 | 2 | 3 | 0 |
| BNA | 1 | 4 | 0 | 0 | 3 | 1 |
| BOI | 0 | 2 | 0 | 0 | 2 | 0 |
| BOS | 0 | 5 | 0 | 0 | 5 | 0 |
| BUF | 1 | 4 | 0 | 1 | 4 | 0 |
| BUR | 2 | 2 | 0 | 1 | 2 | 0 |
| BWI | 0 | 2 | 0 | 0 | 2 | 0 |
| CAE | 1 | 3 | 0 | 1 | 3 | 0 |
| CHA | 1 | 1 | 0 | 1 | 1 | 0 |
| CHS | 2 | 3 | 0 | 2 | 3 | 0 |
| CLE | 3 | 5 | 0 | 3 | 5 | 0 |
| CLT | 0 | 2 | 0 | 0 | 2 | 0 |
| CMH | 0 | 2 | 0 | 0 | 2 | 0 |
| COS | 1 | 3 | 0 | 1 | 3 | 0 |
| CVG | 0 | 3 | 0 | 0 | 3 | 0 |
| DAB | 0 | 2 | 0 | 0 | 2 | 0 |
| DAL | 0 | 2 | 0 | 0 | 2 | 0 |
| DAY | 1 | 4 | 0 | 1 | 4 | 0 |
| DCA | 3 | 3 | 0 | 2 | 3 | 0 |
| DEN | 0 | 6 | 0 | 0 | 6 | 0 |
| DFW | 0 | 4 | 0 | 0 | 4 | 0 |
| DLH | 2 | 3 | 0 | 1 | 3 | 0 |
| DSM | 0 | 3 | 0 | 0 | 3 | 0 |
| DTW | 2 | 4 | 1 | 2 | 2 | 3 |
| DVT | 1 | 0 | 0 | 0 | 0 | 0 |
| ELP | 0 | 1 | 0 | 0 | 1 | 0 |
| EUG | 3 | 3 | 0 | 2 | 3 | 0 |
| EWR | 0 | 1 | 0 | 0 | 1 | 0 |
| EYW | 2 | 2 | 0 | 2 | 2 | 0 |
| FAI | 0 | 1 | 0 | 0 | 1 | 0 |
| FAT | 0 | 1 | 0 | 0 | 1 | 0 |
| FLL | 1 | 4 | 2 | 1 | 4 | 2 |
| FWA | 2 | 3 | 0 | 0 | 2 | 1 |
| FXE | 1 | 1 | 0 | 1 | 1 | 0 |
| GEG | 2 | 2 | 0 | 1 | 2 | 0 |
| GRR | 2 | 6 | 0 | 0 | 4 | 2 |
| GSO | 0 | 1 | 0 | 0 | 1 | 0 |
| GSP | 0 | 1 | 0 | 0 | 1 | 0 |
| HNL | 4 | 6 | 0 | 4 | 6 | 0 |
| HOU | 1 | 4 | 0 | 1 | 4 | 0 |
| HPN | 0 | 2 | 0 | 0 | 2 | 0 |
| HSV | 0 | 3 | 0 | 0 | 3 | 0 |
| IAD | 0 | 5 | 0 | 0 | 5 | 0 |
| IAH | 0 | 2 | 0 | 0 | 2 | 0 |
| ICT | 1 | 3 | 0 | 1 | 3 | 0 |
| ILN | 0 | 3 | 0 | 0 | 3 | 0 |
| IND | 0 | 3 | 0 | 0 | 3 | 0 |
| ISP | 1 | 3 | 0 | 0 | 2 | 1 |
| JAN | 0 | 1 | 2 | 0 | 1 | 2 |
| JAX | 0 | 3 | 0 | 0 | 3 | 0 |
| JFK | 0 | 4 | 0 | 0 | 4 | 0 |
| JNU | 2 | 2 | 0 | 2 | 2 | 0 |
| LAS | 2 | 3 | 0 | 1 | 2 | 1 |
| LAX | 0 | 2 | 0 | 0 | 2 | 0 |
| LCK | 0 | 1 | 0 | 0 | 1 | 0 |
| LGA | 1 | 2 | 0 | 1 | 2 | 0 |
| LGB | 2 | 4 | 0 | 2 | 4 | 0 |
| LIT | 2 | 4 | 0 | 2 | 4 | 0 |
| MCI | 0 | 3 | 0 | 0 | 3 | 0 |
| MCO | 1 | 2 | 0 | 0 | 2 | 0 |
| MDT | 0 | 2 | 0 | 0 | 2 | 0 |
| MDW | 3 | 6 | 0 | 3 | 6 | 0 |
| MEM | 0 | 3 | 1 | 0 | 3 | 1 |
| MHT | 1 | 4 | 0 | 1 | 4 | 0 |
| MIA | 3 | 8 | 0 | 2 | 7 | 1 |
| MKE | 2 | 1 | 0 | 2 | 1 | 0 |
| MMU | 1 | 1 | 0 | 1 | 1 | 0 |
| MSP | 0 | 1 | 0 | 0 | 1 | 0 |
| MSY | 1 | 3 | 0 | 1 | 3 | 0 |
| OAK | 1 | 3 | 0 | 0 | 2 | 1 |
| OKC | 2 | 5 | 0 | 2 | 5 | 0 |
| OMA | 0 | 3 | 0 | 0 | 3 | 0 |
| ONT | 0 | 1 | 0 | 0 | 1 | 0 |
| ORD | 0 | 7 | 0 | 0 | 7 | 0 |
| ORF | 0 | 2 | 0 | 0 | 2 | 0 |
| PBI | 2 | 4 | 0 | 2 | 4 | 0 |
| PDX | 0 | 1 | 2 | 0 | 1 | 2 |
| PHL | 0 | 4 | 0 | 0 | 4 | 0 |
| PHX | 0 | 5 | 0 | 0 | 5 | 0 |
| PIE | 5 | 6 | 0 | 1 | 2 | 4 |
| PIT | 0 | 2 | 0 | 0 | 2 | 0 |
| PVD | 1 | 3 | 0 | 1 | 3 | 0 |
| RDU | 0 | 2 | 0 | 0 | 2 | 0 |
| RFD | 2 | 3 | 0 | 1 | 2 | 1 |
| RIC | 2 | 4 | 0 | 2 | 4 | 0 |
| RNO | 1 | 2 | 0 | 1 | 2 | 0 |
| ROC | 1 | 3 | 0 | 1 | 3 | 0 |
| RSW | 0 | 2 | 0 | 0 | 2 | 0 |
| SAN | 1 | 1 | 0 | 1 | 1 | 0 |
| SAT | 0 | 2 | 0 | 0 | 2 | 0 |
| SDF | 0 | 2 | 0 | 0 | 2 | 0 |
| SEA | 0 | 2 | 0 | 0 | 2 | 0 |
| SFB | 2 | 4 | 0 | 2 | 4 | 0 |
| SFO | 0 | 1 | 0 | 0 | 1 | 0 |
| SHV | 2 | 3 | 0 | 1 | 3 | 0 |
| SJC | 4 | 6 | 0 | 3 | 5 | 1 |
| SLC | 0 | 2 | 0 | 0 | 2 | 0 |
| SMF | 0 | 3 | 0 | 0 | 3 | 0 |
| SNA | 1 | 2 | 0 | 1 | 2 | 0 |
| STL | 0 | 4 | 0 | 0 | 4 | 0 |
| SWF | 1 | 2 | 0 | 1 | 2 | 0 |
| SYR | 1 | 3 | 0 | 1 | 3 | 0 |
| TEB | 2 | 3 | 0 | 2 | 3 | 0 |
| TLH | 0 | 3 | 0 | 0 | 3 | 0 |
| TPA | 1 | 1 | 2 | 1 | 1 | 2 |
| TRI | 1 | 2 | 0 | 0 | 2 | 0 |
| TUL | 1 | 3 | 0 | 1 | 3 | 0 |
| TUS | 1 | 1 | 0 | 0 | 0 | 1 |
| TYS | 0 | 1 | 0 | 0 | 1 | 0 |
| VNY | 1 | 2 | 0 | 1 | 2 | 0 |
| Total | 104 | 331 | 10 | 79 | 314 | 27 |

# Notes and References

# Endnotes

See Appendix L for a listing of acronym used in this report.

See Appendix A for the selection criteria, as well as a listing and map of these 121 airports.

Rovinsky, Dr. Robert. (1999, September 25). Satellite Navigation Investment Analysis Report. Federal Aviation Administration, 1-129. Retrieved May 18, 2004 from World Wide Web: (http://www.faa.gov/asd/satnav/fullyrelease.pdf).

Gustafson, David M., Smith, Alexander E., Cassell, Rick. (October 1998). Cost Benefit Analysis of the Combined WAAS/LAAS System. AIAA Digital Avionics Systems Conference, 1-8. Retrieved May 18, 2004 from World Wide Web: (http://www.aviationtoday.com/reports/costbenefit.pdf)

Prabhakar, Anand S. (1996). Economic Analysis of Local Area Augmentation System and Alternative Architectures (Rep. No. A560803). Massachusetts: Transportation Systems Center.

No Author. (1997). Local Area Augmentation System Cost Savings Potential. Washington, DC: Air Transport Association.

See Appendix F.

LAAS Benefits Analysis - Executive Summary of the Navigation Capabilities Baseline, IBM Corporation, November 2003.

LAAS Benefits Analysis - Executive Summary of the LAAS Incremental Capabilities, IBM Corporation, December 15, 2003.

The National Economic Impact of Civil Aviation; DRI-WEFA, Inc.; July 2002; p.22. (http://www.gama.aero/dloads/DRI-WEFA_EconomicImpactStudy.pdf)

After discussions with air cargo operators, a simple approach was developed in which the Box Value of Time is represented as a function of the fraction of time-sensitive cargo on each delayed aircraft that is at risk of arriving late.  Delays less than 30 minutes were considered to be inconsequential, and the fraction of “late” cargo increased from 0% at 30 minutes of delay to 100% at 1 hour of delay.  Multiplying this fraction by the average value of time-sensitive cargo onboard a typical flight (($40k; derived from publicly available annual reports of relevant air cargo carriers) allows the calculation of the Box Value of Time associated with any length of delay.

See Appendix R for a listing of these required ILS installations by airport.

Radio Spectrum Plan (2003 Revision) ATO-W; p 53 “Until there is a meaningful de-commissioning of at least some VORs, it may be difficult to implement LAAS installations in this band beyond the present plan of 161 stations.”

FAA Radio Spectrum Plan (2003 Revision) ATO-W; p 55 “Spectrum resources are expected to be available to implement some additional ILS systems in lower traffic density areas of CONUS. However, it would be extremely difficult, perhaps impossible, to make further ILS frequency assignments in some high traffic density areas, such as the New York City area.”

See for example: Handbook of Airline Economics: Chapter 39 Airline Irregular Operations, or

Diversion Cost Calculations, http://www.passur.com/pst/report_app_a.htm, or

FAA/APO – Schedule Disruptions Version 2, pg 3 and Table 4, pg 11, http://apo.faa.gov/arcc/Issue%20Papers/031215%20Schedule%20Disruptions.doc, or

Airbus, Economic Impact – Diversion Recovery Plan, http://apo.faa.gov/arcc/030916%20Meeting/Handouts/6, or

Zalman, Shavell A. (2000, April 15). The Effects of Schedule Disruptions on the Economics of Airline Operations. The MITRE Corporation, 1-11.

a) Beatty, R., Hsu, R., Berry, L, and Rome, J. (Dec. 1998) Preliminary Evaluation of Flight Delay Propagation Through an Airline Schedule; 2nd USA/Europe Air Traffic Management R&D Seminar.

b) Rome, J, Rose, S, Lee, R, Cistone, J, Bell, G., Leber, W. (undated) Ripple Delay and Its Mitigation.

c) No Author, Nov 2003, Investment Analysis Benefit Guidelines: Quantifying Benefits from Projected Reductions in National Airspace System Equipment Outages; FAA ASD-430; Appendix A, p. A-3.

d) Welch, Andrews and Robinson, Aug 2001, Assessing Delay Benefits of the Final Approach Spacing Tool, MIT Lincoln Labs, and NASA Ames Research Center, presented at the AAIA Guidance, Navigation and Control Conference, Aug 2001.

No Author. (2004, March). FAA Aerospace Forecast 2004-2015. Federal Aviation Administration, Chapter 1.  http://www.api.faa.gov/foreca03/start.htm

See Appendix K for details on data sources.

Also, see Appendix G for a short list of sites outside of the 121 studied airports that were identified by airline representatives as potentially important sites for LAAS benefits.

No Author. (1992, October 29). Guidelines and Discount Rates for Benefit-Cost Analysis of Federal Programs. Office of Management and Budget

See Appendix F.

Hawkins, Joseph A. (1983, September). Establishment and Discontinuance Criteria for Precision Landing Systems. US Department of Transportation and The Federal Aviation Administration, 1-102. Retrieved May 18, 2004 from the World Wide Web: http://api.hq.faa.gov/precision%20landing%20systems/Precision%20Landing%20Systems.pdf

Haro, Pablo; Mateo, Mariluz de; Andrada, Luis. (1998, October 7). Methodology and Quantification of Several EGNOS Operational Benefits. Ministry of Public Works and the Economy, 1-6. Retrieved May 18, 2004 from the World Wide Web.

http://www.mfom.es/aviacioncivil/programas/egnos_html/cba.doc

See for example: a) Pervan, Boris; Lawrence, David; Gromov, Konstantin. (1998, March 19). Flight Test Evaluation of a Prototype Local Area Augmentation System Architecture. Department of Aeronautics and Astronautics, 1-9. Retrieved May 18, 2004 from the World Wide Web: http://waas.stanford.edu/~wwu/papers/gps/PDF/flight_eval_laas_bsp97.pdf

b) Hammer, Jonathan. (2000). Case Study of Paired Approach Procedure to Closely Spaced Parallel Runways. The MITRE Corporation, 223-252. Retrieved May 18, 2004 from the World Wide Web: http://www.mitre.org/work/best_papers/best_papers_00/hammer_casestudy/hammer_casestudy.pdf

http://www.transtats.bts.gov/

http://www.faa.gov/ats/asc/capacity.html

Hawkins, Joseph A. (1983). Establishment and Discontinuance Criteria for Precision Landing Systems (Rep. No. FAA-APO-83-10). Washington, DC: Federal Aviation Administration.

Prabhakar, Anand S. (1996). Economic Analysis of Local Area Augmentation System and Alternative Architectures (Rep. No. A560803). Massachusetts: Transportation Systems Center.

FAA Aviation Policy and Plans; Airway Planning Standard Number One Terminal Air Navigation Facilities and Air Traffic Control Services: http://apo.faa.gov/7031/7031.pdf

NCDC data provided by ASD-400.

For FedEx’s Memphis hub and UPS’s Louisville hub, the entire 24 hour time period was used since they have continual traffic throughout the night.

The period from 9/11/01 through 12/31/01 was omitted.  Disruptions due to labor strikes were also omitted.

For a discussion of the impact of severe weather on airline operations, see for example, Zalman, Shavell A. (2000, April 15). The Effects of Schedule Disruptions on the Economics of Airline Operations. The MITRE Corporation, 1-11. Retrieved May 18, 2004 from the World Wide Web: http://www.mitre.org/work/tech_papers/tech_papers_00/shavell_effects/shavell_effects.pdf

For details see FAA Advisory Circulars 120-29A, 120-28D; FAA Order 8400.10

See Appendix E for a description of how total demand is estimated.

Capacity data was made available to IBM by the FAA’s ASD-400

See Appendix E for a description of how a “typical” day’s traffic is estimated

See Appendix E  for a description of the Single Airport Delay Model.

See Appendix C.

Boeing (RNP Capability of the FMC-Equipped 737, Generation 3, Figure 6.1-1)

Becher, T.; Formosa, J. (2000, June 16). RNAV Near-Term Terminal Procedures Development. Center for Advanced Aviation System Development, 1-11. Retrieved May 19, 2004 from the World Wide Web: http://www.mitrecaasd.org/library/presentations/becher.pdf

Hoitomt, Debra; Dareing, Stephen; Tang, Baoxing. (No Date Given). Traffic Management and Airline Operations. United Airlines Research Center, 1-3. Retrieved May 19, 2004 from the World Wide Web: http://icat-server.mit.edu/~fcarr/ACC2002/Abstracts/UAL_Hoitomt.pdf

Knorr, David. (2000, June 16). The Operational Assessment of Free Flight Phase 1 ATM Capabilities. Free Flight Phase 1 Program Office, 1-9. Retrieved May 19, 2004 from the World Wide Web: http://www.mitrecaasd.org/library/presentations/blucher.pdf

See for example:  a) Testimony before the Aviation Subcommittee of the House Committee on Transportation and Infrastructure, (1999, October 14).  http://www.house.gov/transportation/aviation/hearing/10-14-99/chew.html

b) No Author. (1998, November 18). All-Airline Meeting. CNS/ATM Focused Team (C/AFT), 1-24. Retrieved May 19, 2004 from the World Wide Web: http://www.boeing.com/commercial/caft/reference/meetings/98_11_18/01_atspfg.pdf

c) Pepper, Joshua W.; Mills, Kristine R.; Wojcik, Leonard A. (2003, June 27). Predictability and Uncertainty in Air Traffic Flow Management. Center for Advanced Aviation System Development (CAASD), 1-10. Retrieved May 19, 2004 from the World Wide Web: http://www.mitrecaasd.org/library/presentations/atm2003/atm2003_paper45.pdf

d) this benefit has also been strongly substantiated in IBM’s interviews with airline representatives.

No Author. (2003, September 11). FAA Flight Plan 2004-2008. Federal Aviation Administration, 31. Retrieved May 19, 2004 from World Wide Web: http://www.faa.gov/apo/strategicplan/FAA_Flight_Plan.pdf

(25 Feb, 2004) IBM LAAS Benefits Analysis – Preliminary Findings.

No Author. (No Date Given). Section 6. Holding Aircraft. Federal Aviation Administration. Retrieved May 19, 2004 from the World Wide Web: http://www.faa.gov/ATPUBS/ATC/Chp4/atc0406.html

Interview with a major carrier produced the estimate of 2 minutes to taxi 1500 ft

No Author. (No Date Given). Section 3. Wake Turbulence. Federal Aviation Administration. Retrieved May 19, 2004 from the World Wide Web: http://www2.faa.gov/ATpubs/AIM/Chap7/aim0703.html

Odoni, Amedeo R., Rousseau, Jean-Marc, and Wilson, Nigel (1994). Models in Urban and Air Transportation. Amsterdam: Elsevier Science Publishers.

See Appendix E for a description of how a “typical” day’s traffic is estimated.

See Appendix C.

Estimated to be 30 departures per hour, based on theoretical models and comparison to similar runways at other airports.

Critical area holds were identified using taxiway diagrams for the airports studied.

See Appendix C.

Egan, Paul. (2001, February 27). New radar would speed airport traffic. The Detroit News. Retrieved May 19, 2004 from the World Wide Web: http://www.detnews.com/2001/metro/0102/27/d01-193153.htm

Houck, Sharon; Barrows, Andrew; Parkinson, Bradford; Enge, Per; Powell, J. David. (1999). Flight Testing WAAS for Use in Closely Spaced Parallel Approaches. Department of Aeronautics and Astronautics, Stanford University, 1-12. Retrieved May 19, 2004 from the World Wide Web: http://waas.stanford.edu/~wwu/papers/gps/PDF/sharonparallel.pdf

Houck, Sharon; Powell, J. David. (2001). Assessment of the Probability of a Midair Collision during an Ultra Closely Spaced Parallel Approach. Department of Aeronautics and Astronautics, Stanford University, 1-11. Retrieved May 19, 2004 from the World Wide Web: http://waas.stanford.edu/~wwu/sharon/briefs/gncpaper01.pdf

Houck, Sharon. (2001, April). Multi Aircraft Dynamics, Navigation and Operation. The Department of Aeronautics and Astronautics and the Committee on Graduate Studies of Stanford University, 1-141. Retrieved May 19, 2004 from the World Wide Web: http://waas.stanford.edu/~wwu/sharon/briefs/sharonthesis01.pdf

Ashford, Rose. (1998, December 24). Closely Spaced Parallel Approaches. NASA Ames Research Center. Retrieved May 19, 2004 from the World Wide Web: http://www.asc.nasa.gov/tap/cspa/cspa.html

Elliott Dawn M. and Perry R. Brad. (2000, August14-17). NASA Research for Instrument Approaches to Closely Spaced Parallel Runways. NASA, 1-8. Retrieved June 2, 2004 from the World Wide Web: http://techreports.larc.nasa.gov/ltrs/PDF/2000/aiaa/NASA-aiaa-2000-4358.pdf

Ashford, Rose. (2002, September 11). Closely-Spaced Parallel Approaches. NASA, 1-21. Retrieved May 19, 2004 from the World Wide Web: http://human-factors.arc.nasa.gov/ihi/personnel/ashford/CSPA20D.pdf

Eurocontrol. (2003, May 2). GBAS Roadmap. EUROCONTROL, 1-6. Retrieved May 19, 2004 from the World Wide Web:

http://www.eurocontrol.fr/projects/sbas/Library/gwg7/GWG-7_IP1_GNSS.4WP.yy2_v1.0.pdf

Eurocontrol, “Benefit Estimation of GBAS for Simultaneous Independent Operations for Closely Spaced Parallel Runways in ECAC”

Eurocontrol, Executive Summaries of ECAC Precision Approach and Landing Task Force (EPAL) Activities in Close Relation to GBAS, Joint EPAL/GWG meeting, February 3, 2004.

Shank, E. M.; Hollister, K. M. (1994). Precision Runway Monitor. Lincoln Laboratory Journal,

Vol. 7, No. 2.

Haines, Dr. A. L.; Swedish, W. J. (1981). Requirements for Independent and Dependent Parallel Instrument Approaches at Reduced Runway Spacing (Rep. No. MTR-81W15). Virginia: The MITRE Corporation.

Bone, R.; Olmos, O.; Mundra, A. (2001). Paired Approach:  A Closely Spaced Parallel Runway Approach Concept (Rep. No. MP-01W0000046). Virginia: The MITRE Corporation.

Higgins, M. K. (1994). Evidence for Parallel Approach Blunders in the National Airspace System Incident Monitoring System (NAIMS). (Rep. No. MP-94W000076). Virginia: The MITRE Corporation.

Monaco, Nadine. (2003, September). New Performance-based Navigation Standards Encourage Increased Flexibility and Safety in the Skies. Federal Aviation Administration. Retrieved June 2, 2004 from the World Wide Web: http://www.mitre.org/news/digest/aviation/09_03/a_nrp.html

Mundra, Anand, D., Cooper, Wayne W., Levy, Benjamin S., Lunsford, Clark R., Smith, Arthur P., Tittsworth, Jeffrey A. and Lang, Steven. (2003, June 23-27). A Phased Approach to Increase Airport Capacity Through Safe Reduction of Existing Wake Turbulence Constraints. The MITRE Corporation. Retrieved June 2, 2004 from the World Wide Web: http://atm2003.eurocontrol.fr/slides/airport/6_85_Cooper.ppt

Houck, Sharon; Barrows, Andrew; Parkinson, Bradford; Enge, Per; Powell, J. David. (1999). Flight Testing WAAS for Use in Closely Spaced Parallel Approaches. Department of Aeronautics and Astronautics, Stanford University, 1-12. Retrieved May 19, 2004 from the World Wide Web: http://waas.stanford.edu/~wwu/papers/gps/PDF/sharonparallel.pdf

Salvano, D. (2003, August 12). ADS-B within the Safe Flight 21 Program. Federal Aviation Administration. Retrieved June 2, 2004 from the World Wide Web: http://www.faa.gov/And/AND500/docmgr/docs/T0276.ppt

No Author. (No Date Given). 2002 Aviation Capacity Enhancement Plan. Federal Aviation Administration. Retrieved June 2, 2004 from the World Wide Web: http://www.faa.gov/ats/asc/02ACE.html

FAA (2001) Airport Capacity Benchmark Report 2001

Capacities for JAN were unavailable.  Values from RDU were substituted based on similarities in the runway layouts and centerline separations.

See for example, www.eurocontrol.fr/projects/sbas/ Library/gwg7/GWG_7_WP05_GBAS-Datalink.pdf

Emergency Disaster Management Inc. 25, March, 2001. “Runway overruns/sliding off” (http://www.emergency-management.net/runway_acc.htm)

BBC New. 29, October, 2002. “Plane overruns airport taxiway”. (http://news.bbc.co.uk/1/hi/england/2373727.stm)

Aviation Safety Network, Accident Description. 25-Jan-2002.  ANC Incident Description for China Airlines Airbus A340. (http://aviation-safety.net/database/2002/020125-0.htm)

AOPA Online. 3-Sept, 2002. “Runway Incursion Analysis, ORD, Boeing 737 (B737), Unknown Ground Vehicle” (http://www.aopa.org/asf/incursions.html)

Number derived from the following FAA website (http://www.api.faa.gov/strategic/docs/sup-sys-40-arpaccessgoal.html).

FAA Navigation & Landing Transition Strategy Report  (http://www1.faa.gov/asd/briefings/NavReport8-02.pdf).

Khatwa R, Helmreich R, Analysis of Critical Factors During Approach and Landing in Accidents and Normal Flight, Flight Safety Digest, Volume 17, No 11-12, Flight Safety Foundation, Alexandria, VA, pg 80.

Enders et al, Airport Safety: A Study of Accidents and Available Approach-and-landing Aids, Flight Safety Digest, Flight Safety Foundation, Alexandria, VA., March 1996.

Nordwall B D, U.S. Changing to One Type of Instrument Approach, Aviation Week and Space Technology, July 8th, 2002 pg 45-46.

FAA. (2002). The National Aviation Safety Data Analysis Center. (https://extranet.nasdac.faa.gov)

Statistical Package for the Social Sciences.

NTSB accident briefs can be obtained at the NTSB’s web site  (http://www.ntsb.gov/ntsb/query.asp).

Remarks for the Honorable Norman Y. Mineta Secretary of Transportation. (January 27, 2004). Securing America’s Place as Global Leader in Aviation’s Second Century (http://www.jpo.aero/mineta%20speech%20012704.pdf).

FAA Flight Plan 2004-2008, p34; (http://www2.faa.gov/apo/strategicplan/FAA_Flight_Plan.pdf).

ICASC – Local Area Augmentation System,  (http://avnwww.jccbi.gov/icasc/gnss_laas.html).

FAA. (June 2003). Flight Schedule Data Systems (FSDS),  In June 2003 there were 182 foreign airports with scheduled arrivals from a domestic carrier, (http://www.apo.data.faa.gov/).

AIN Online. (2002). Europeans Embrace MLS with a vengeance. (http://www.ainonline.com/issues/04_01/Apr_2001_europeanmlspg75.html).

Estimated using FAA/APO FSDS (http://www.apo.data.faa.gov).

FAA’s Office of Environment and Energy Noise Division; (http://www.aee.faa.gov/noise/Aircraft_Noise.htm).

US DoT. (Thursday, April 22, 2004).  U.S. DOT Commemorates Earth Day with Announcement of $307 Million Effort to Combat Noise Pollution Near Airports.  (http://www.dot.gov/affairs/dot5404.htm).

Leqve, Chad E., Manager, MSP Aviation Noise & Satellite Programs (Oct 1, 2003).  Minneapolis/St. Paul International Airport GPS/LAAS Initiatives. GBAS/LAAS User Group Meeting.

Chicago Department of Aviation. (1996). ORD Noise Mitigation Program. (http://www.flychicago.com/cnrc/cnrc.shtm).

Boeing Airport Noise Regulations; DEN; (http://www.boeing.com/commercial/noise/denver.html).

Boeing Airport Noise Regulations; BOS; (http://www.boeing.com/commercial/noise/logan.html).

U.S. GAO, Aviation and the Environment, FAA’s Role in Major Noise Programs (http://www.transource.org/Shared_files/gaonoise.pdf)

Airport Report Express, Vol 6, No. 77, Sept 23, 1996: California Airports Gain $84 Million (http://www.airportnet.org/depts/publications/express/1996HTM/9-23-96.htm)

Airport Report Express, Vol 6, No. 77, Sept 23, 1996: California Airports Gain $84 Million. (http://www.airportnet.org/depts/publications/express/1996HTM/9-23-96.htm)

Airport Report Express, Vol 6, No. 77, Sept 23, 1996: California Airports Gain $84 Million. (http://www.airportnet.org/depts/publications/express/1996HTM/9-23-96.htm)

NY State 2003 Annual Report Aviation Section 5: Airport Funding: Table I – AIR ’99 Aviation Grant Status Report (http://www.dot.state.ny.us/pubtrans/files/2003_annual_report_aviation_sect5.pdf)

NY State 2003 Annual Report Aviation Section 5: Airport Funding: Table I – AIR ’99 Aviation Grant Status Report (http://www.dot.state.ny.us/pubtrans/files/2003_annual_report_aviation_sect5.pdf)

NY State 2003 Annual Report Aviation Section 5: Airport Funding: Table I – AIR ’99 Aviation Grant Status Report (http://www.dot.state.ny.us/pubtrans/files/2003_annual_report_aviation_sect5.pdf)

Airport Report Express, Apr 29, 1998: Illinois Airports Receive AIP Grants (http://www.airportnet.org/depts/publications/express/1998HTM/4-29-98.htm)

Airport Report Express, Apr 29, 1998: Illinois Airports Receive AIP Grants (http://www.airportnet.org/depts/publications/express/1998HTM/4-29-98.htm)

Airport Report Express, Vol 6, No. 77, Sept 23, 1996: California Airports Gain $84 Million (http://www.airportnet.org/depts/publications/express/1996HTM/9-23-96.htm)

Denver Must Pay County Four Million for Airport Noise (http://www.netvista.net/~hpb/news/oct-30.html)

Florida Landowners Must Prove Decreased Property Value in Airport Noise Suit (http://www.netvista.net/~hpb/news/apr-3.html)

Lawyers Hired to Fight Noise at Newark International Airport (http://www.netvista.net/~hpb/news/mar-20a.html)

Court Lets City Go to Trial on Noise Impact Issue (http://www.netvista.net/~hpb/news/feb-24.html)

Memphis Airport Authority Votes to Settle Class-Action Noise Lawsuit (http://www.netvista.net/~hpb/news/june27.html)

Minnesota City Sues Airport Commission Over Shifting Jet Noise to Their Community

(http://www.netvista.net/~hpb/news/june-11.html)

More Schools to Be Insulated As a Result of Lawsuit over Aircraft Noise in Chicago (http://www.netvista.net/~hpb/news/nov-6.html)

School to Sue for Soundproofing from Airport Noise (http://www.netvista.net/~hpb/news/dec-10.html)

Connecticut Residents Threaten to Sue State If Airport Noise Isn't Reduced (http://www.netvista.net/~hpb/news/oct-2.html)

Boeing Airport Noise Regulations; (http://www.boeing.com/commercial/noise/usa_list.html)

FAA, Advisory Circular 91-36C (Oct 19, 1984). Visual Flight Rules (VFR) Flight Near Noise Sensitive Areas. (http://www.netvista.net/~hpb/ac-91-36.html).

WRF. (February, 1999).  Recipients Of Federal Airport Improvement Grants May Not Impose Discriminatory Conditions On Corporate Aircraft Operators Or Similar Airport Users.  (http://www.wrf.com/publications/publication.asp?id=1252309172000).

MassPort, Logan Airport. (2004.)  Airport Programs, Environmental. (http://www.massport.com/logan/airpo_noise_gloss.html).

Cincinnati/Northern Kentucky International Airport.  Community and Environment. (http://www.cvgairport.com/airport/enviro/noise.shtml).

Satellite Navigation Product Teams. Airport Benefit: Noise Abatement Areas/Environmentally-Sensitive Areas.  (http://gps.faa.gov/Programs/waas/airports-text.htm).

Seattle Tacoma International Airport, Washington, (Approved on 6/3/02). The Noise Compatibility Plan (NCP). (http://www.faa.gov/arp/app600/14cfr150/roas/ROAsea02.htm).

NBAA. (August 27, 2004).  Flight Restrictions for 2004 Republican National Convention in New York City. (http://web.nbaa.org/public/ops/airspace/restrictions/2004/rnc/).

EAA News. (2004). ADIZ added for New York city area; other airspace restrictions announced include theme parks. (http://www.eaa.org/communications/eaanews/030318_adiz.html).

EAA News. (2004). ADIZ added for New York city area; other airspace restrictions announced include theme parks. (http://www.eaa.org/communications/eaanews/030318_adiz.html).

AOPA. (2004). Presidential movement TFRs. (http://www.aopa.org/whatsnew/notams.html#4/7295).

EAA News. (March 22, 2003). Chicago mayor gets his way; EAA decries TFR in Chicago. (http://www.eaa.org/communications/eaanews/030322_tfr_Chicago.html).

AOPA. (Dec 7, 2001). FAA unveils major airspace restrictions for SLC Winter Olympics, Salt Lake City-area GA pilots will be grounded for 19 days. (http://www.aopa.org/whatsnew/newsitems/2001/01-4-199x.html).

Aviation During the Olympics. (Update 7/18/96). Temporary Flight Restrictions (TFRs) include two in Downtown Atlanta. (http://www.mindspring.com/~cavu/olympics.html#TFRs).

AivNav. (http://www.airnav.com)

Homan, Ph.D, Anthony C. (January 200). Improved Methods for Measuring the Benefits of Air Traffic Control Improvements (Paper No. 00-0573).  Center for Advanced Aviation System Development.

FAA (May 31, 2002).  FAA Order 5100.38B, Airport Improvement Program Handbook, Chapter 1.  Introduction, Section 1.  General. 21. Revenue Sources. (http://www.faa.gov/arp/aip/order/5100-38B1.htm#c1p21).

Satellite Operational Implementation Team. (2002, August 5). LAAS Concept of Operations; “Each LAAS ground facility has a very high frequency data broadcast (VDB) coverage volume that extends from surface line of sight to 10,000ft above ground level (AGL) at a radial distance out to 23 nm from the VDB antenna site.”

National Flight Data Center, FAA ATA-110; http://www.faa.gov/ats/ata/ata100/110/index.html

See Appendix I, assumptions 3 and 4.

GRA Incorporated Aviation Specialist Group Inc., and Database Products. (2004, May 28). Economic Values for FAA Investment and Regulatory Decisions, A Guide. Final Report prepared for FAA Office of Aviation Policy and Plans. Retrieved May 28, 2004 from the World Wide Web: http://apo.faa.gov/arcc/Research.htm.

Treatment of Values of Passenger Time in Economic Analysis, U.S. Department of Transportation, FAA-APO-03-1, March 2003. Retrieved May 28, 2004 from the World Wide Web: http://apo.faa.gov/arcc/Research.htm.

GRA Incorporated Aviation Specialist Group Inc., and Database Products. (2004, May 28). Economic Values for FAA Investment and Regulatory Decisions, A Guide. Final Report prepared for FAA Office of Aviation Policy and Plans. Retrieved May 28, 2004 from the World Wide Web: http://apo.faa.gov/arcc/Research.htm.

DOT TranStats ASQP Glossary: “Arrival delay equals the difference of the actual arrival time minus the scheduled arrival time. A flight is considered on-time when it arrives less than 15 minutes after its published arrival time.” http://transtats.bts.gov/Glossary.asp?index=A

See for example: Press, Flannery, Teukolsky, Vetterling, Numerical Recipes, Cambridge Univ. Press, 1986; or, http://www.ualberta.ca/~cdeutsch/images/Lec04-MonteCarlo.pdf.; or, Rubinstein, Simulation and the Monte Carlo Method, Wiley Interscience, 1981.

With replacement, the sampling may result in random numbers being selected more than once within the same trial. In other words, randomly selecting a particular quarter hour to add a flight to does not eliminate that quarter hour from being selected again. Thus, more than one flight may be added to any one quarter hour interval. See, for example: http://www.nysscpa.org/cpajournal/2002/0402/dept/d045802.htm.

NCDC data provided by ASD-400.

Visual weather is considered when visibility is equal or above 3miles and ceiling is equal or above 1000ft. Visibility and/or ceilings below these limits are considered IMC conditions.

ASD-400: Airport Survey and Future Capacity files

FAA Office of System Capacity: http://www.faa.gov/ats/asc/capacity.html

See for example, http://www.landrum-brown.com/MasterPlans/PVD/facility-req-chapter3/images/exh%20III-1-9.pdf

A minimum runway length requirement of 4,200 feet, based on the minimum length required for a precision approach runway, is also included.

D10: McDonellDouglas DC-10; B757: Boeing 757; B737: Boeing 737; M80: McDonellDouglas MD80; CRJ: Canadair Regional Jet; BE1: Beechcraft 1900; CNA: Cessna Light Aircraft; PAG: Piper Light Aircraft

Exceptions to this are discussed in the Benefits for Closely Spaced Parallel Approaches section.

FAA Aviation Policy, Planning and Environment; Establishment and Discontinuance Criteria for Precision Landing Systems:  http://api.hq.faa.gov/precision%20landing%20systems/Precision%20Landing%20Systems.pdf

FAA Aviation Policy and Plans; Airway Planning Standard Number One Terminal Air Navigation Facilities and Air Traffic Control Services: http://apo.faa.gov/7031/7031.pdf

The table shows results for the Heavy Equipment category.  Since these CMH runways are longer than the maximum runway length requirement (see Table 3), all categories will have the same runway utilization.

FAA Office of System Capacity: http://www.faa.gov/ats/asc/publications/CAPACITY/CMH.pdf

Beatty, R., Hsu, R., Berry, L, and Rome, J. (Dec. 1998) Preliminary Evaluation of Flight Delay Propagation Through an Airline Schedule; 2nd USA/Europe Air Traffic Management R&D Seminar.

Welch, Andrews and Robinson, Aug 2001, Assessing Delay Benefits of the Final Approach Spacing Tool, MIT Lincoln Labs, and NASA Ames Research Center, presented at the AAIA Guidance, Navigation and Control Conference, Aug 2001.

No Author, Nov 2003, Investment Analysis Benefit Guidelines: Quantifying Benefits from Projected Reductions in National Airspace System Equipment Outages; FAA ASD-430; Appendix A, p. A-3.

Rome, J, Rose, S, Lee, R, Cistone, J, Bell, G., Leber, W. (undated) Ripple Delay and Its Mitigation.

See for example, http://www.faa.gov/asd/ia-or/NASPAC.htm, and http://www.tc.faa.gov/acb300/330_naspac.asp

http://www.apo.data.faa.gov

This restriction to delays greater than 15 minutes follows the FAA’s definition of delay. For example, from http://www.apo.data.faa.gov, “ASQP Delayed Flight” is defined as “ASQP reported flight that arrive 15 minutes or more after the OAG schedule arrival time.” and “Delayed Gate Arrival” is defined as “Delayed gate arrivals are arriving flights delayed 15 minutes or more when compared to scheduled or flight plan.”

See particularly; Beatty, R., Hsu, R., Berry, L, and Rome, J. (Dec. 1998) Preliminary Evaluation of Flight Delay Propagation Through an Airline Schedule; 2nd USA/Europe Air Traffic Management R&D Seminar.

No Author, Nov 2003, Investment Analysis Benefit Guidelines: Quantifying Benefits from Projected Reductions in National Airspace System Equipment Outages; FAA ASD-430; Appendix A, p. A-3.

# Text boxes

Vertical

Containment

Defined, Repeatable Flight Paths

Departure from 16L

Lateral Containment

LAAS Approach 2

LAAS

Incremental

Capabilities

1

Capabilities of

Systems in the

Baseline

2

LAAS Capabilities

3

LAAS

Incremental

Benefits

LAAS Approach 1

Missed Approach from 16R

Approach to 16R

Approach to 9R

Approach to 4R

Approach to 9L

(3+x)° GS

3° GS

Touchdown

Point

(3+x)° GS

3° GS

Touchdown

Point 2

(RJ, TurboProp, etc)

Touchdown

Point 1

(Heavy Jet)