ICES-401-SPEC-002

Version 1.1

Revision Date:  5-13-99

`

DRAFT

Mission Operations Requirements DOCUMENT (MORD)

FOR THE

ICE, CLOUD & LAND ELEVATION SATELLITE (ICESat)

Goddard Space Flight Center

Greenbelt, Maryland 20771

Signature Page

Prepared/Approved by:

__________________________

Mark Kowaleski,

ICESat Operations Manager

Approved by:

__________________________

Michael Tasevoli,

Mission Systems Engineer

__________________________

William Anselm

Observatory Manager

__________________________

Richard Cassell,

Spacecraft Operations Manager

__________________________

Joe Dezio,

ICESat Project Manager

__________________________

Dolly Perkins,

ESDIS Project Manager

__________________________

James Abshire,

Instrument Scientist

__________________________

Eleanor Ketchum,

Instrument Systems Manager

__________________________

Bob Schutz,

Science Team Leader

David Hancock,

Science Computing Facility Manager

__________________________

Bob Stelmaszek,

Ground Station Manager

__________________________

Timothy Rykowski,

EOS Data Operations System Manager

__________________________

Stan Scott,

Distributed Active Archive Systems Interface Manager

__________________________

Clayton Sigman,

Networks and Security Systems Manager

__________________________

Scott Mitchell,

Flight Dynamics System Manager

__________________________

Peggy Jester,

Instrument Support Facility Manager

Table of Contents

1.	Introduction	6

1.1	Purpose	6

1.2	Document Control	6

1.3	Scope	6

1.4	Document Approach	6

1.5	Document Organization and Requirements Allocation	6

1.6	Applicable Documents	7

2.	Mission Level Requirements	8

2.1	Mission Phases	8

2.2	Mission Data Flow	10

2.3	Mission Operations Documentation	12

2.4	Major Reviews	15

2.5	Mission Operations Development Support	15

2.6	Acceptance and Transition Roles and Responsibilities	15

3.	EOS Polar Ground Stations	17

3.1	Interface Standards	17

3.2	Baseline Ground Station Contact Scenario	17

3.3	Emergency Commanding	18

3.4	Wallops Flight Facility Ground Network Scheduling System	18

3.5	McMurdo Ground Station Support	19

3.6	Doppler Ranging	20

3.7	S-band Command & Telemetry Command Processing	20

3.8	Compatibility Test Van Support	20

3.9	Communications Links Testing	20

4.	Ground Communications	21

4.1	Mission Operations System Communications	21

4.2	Spacecraft Integration & Test Communications	21

4.3	Launch Pad Communications	21

4.4	TDRS Communications	21

4.5	Science Distribution Communications	21

4.6	Communications Testing	21

5.	Mission Operations Center	22

5.1	Mission Communications Support Profile	22

5.2	Major Interfaces	22

5.3	Flight Systems	25

5.4	Facility	25

5.5	Operational Coverage	25

5.6	Database Compatibility	25

5.7	Planning and Scheduling	25

5.8	Real-time Observatory Telemetry Monitoring	25

5.9	Trending Analysis	25

5.10	Observatory Commanding	26

5.11	Remote Monitoring Terminal	26

5.12	Sustaining Engineering	26

5.13	Anomaly Resolution	26

5.14	MOC Data Archive	26

5.15	Laser Flight Safety Operations	26

5.16	Flight Operations Team	27

5.16.1	Staffing and Organization	27

5.16.2	Personnel Availability	27

5.16.3	Emergency and Anomaly Access	27

5.16.4	Training and Certification	27

5.16.5	Rehearsal Support	27

5.17	Reliability	27

5.18	Security	28

5.19	Observatory Integration and Testing Support	28

5.20	Documentation	28

5.21	Reviews and Status Reporting	29

6.	Flight Dynamics System	30

6.1	Mission Characteristics	30

6.2	Software, Hardware, Personnel, and Facilities	31

6.3	Mission Phases Support	31

6.3.1	Maneuver Constraints	31

6.3.2	Pre-Launch Phase	31

6.3.3	Check-out Period Phase	31

6.3.4	Calibration and Validation Phase	32

6.3.5	Maneuver Planning	32

6.3.6	Ground-Track Monitoring and Prediction:	32

6.3.7	Mission Planning Support	32

6.4	Orbit & Attitude Determination	33

6.4.1	Operational Orbit Determination	33

6.4.2	Operational Attitude Support	33

6.5	Sensor Support	33

6.5.1	Sensor Uploadable Parameters Support	33

6.5.2	Sensor Calibration Support	34

6.6	Products Exchange	34

6.6.1	FDS Products to the Mission Operations Center	34

6.6.2	MOC Products to the Flight Dynamics System	34

6.6.3	Flight Dynamics Products to the Science Team	34

6.6.4	Data and Products Archive	35

7.	Instrument Support Facility	36

7.1	Instrument Flight Systems	36

7.2	Facility	36

7.3	Operational Coverage	36

7.4	Planning and Scheduling	36

7.5	Trending Analysis	36

7.6	Sustaining Engineering	36

7.7	Anomaly Resolution	36

7.8	Instrument Operations Team	37

7.8.1	Staffing and Organization	37

7.8.2	Personnel Availability	37

7.8.3	Emergency and Anomaly Access	37

7.8.4	Training and Certification	37

8.	Level Zero Data Processing	38

8.1	General Level Zero Data Processing Functions	38

8.2	EDOS ICESat Mission Performance Reqirements	39

8.3	Data Products Latency Requirements	40

8.3.1	Calibration & Validation Phase Expedited Data	40

8.3.2	Flight Dynamics X-band Data Products	40

9.	Science Data Processing	41

10.	Science Data Archival & Distribution	42

10.1	NSIDC DAAC	42

11.	Spacecraft Contractor Requirements	43

11.1	Engineering Data Archive	43

11.2	Integration & Testing Activities	43

11.3	Sustaining Engineering Support	43

11.3.1	Anomaly Resolution	43

11.3.2	Trending & Analysis	43

11.3.3	Software Maintenance	44

11.3.4	Maintain Flight Software Test Bed	44

12.	GLAS Instrument Developer Requirements	45

12.1	Instrument Operations Training	45

12.2	Documentation	45

12.3	Integration & Testing Activities	45

12.4	On-Orbit Check-out & Transition Activities	45

12.5	Calibration and Validation Support	45

12.6	Engineering Data Archive	46

12.7	Instrument Sustaining Engineering	46

12.7.1	Anomaly Resolution Support	46

12.7.2	Trending & Analysis	46

12.7.3	Software Maintenance	46

13.	Science Team Requirements	47

14.	Appendices	48

14.1	Acronyms	48

14.2	Critical Requirements Allocation Matrix	51

# Introduction

This is the Mission Operations Requirements Document (MORD) for the

Ice, Cloud, & Land Elevation Satellite (ICESat).  This section discusses the purpose, scope, document organization, and applicable documents of this document.

## Purpose

This MORD is derived from the ICESat Mission Systems Requirements Document, February, 1998.  It serves to complete the Ground System Requirements of the Requirements Document Hierarchy, Figure 1, page 1, in terms of mission operations and ground system requirements.

## Document Control

This MORD is maintained under the Configuration Management System of the ICESat Project Office.

The latest version of this document shall be available at the ICESat Homepage at URL:  http://icesat.gsfc.nasa.gov/

Contacts for changes & comments:

Mark M. Kowaleski, ICESat Operations Manager

PHONE:  301-286-7816

EMAIL:  mark.kowaleski@gsfc.nasa.gov

Mike Tasevoli, ICESat System Engineer

PHONE:  301-286-2321

EMAIL:  Michael.Tasevoli.1@gsfc.nasa.gov

## Scope

This MORD details the project-level ICESat mission operations and ground system requirements and is the governing document for the ICESat mission operational development.  This is the controlling document for mission operations and ground system requirements, as well as the operational interactions and agreements required between the major mission elements.

The information in this document encompasses the mission level end-to-end operational requirements and implementation plans and agreements considered necessary to achieve the ICESat mission operationally.  Lower level requirements shall be derived from these requirements by each respective mission element.

## Document Approach

To minimize documentation, this MORD will include requirements for GSFC institutional support traditionally covered in separate documents.  Hence, this document replaces the Detailed Mission Requirements (DMR) document.  In response to this document, the ICESat project shall expect detailed ground system requirements to be derived, documented, and flowed down to the respective subsystems by the organization that the requirements have been allocated to.

## Document Organization and Requirements Allocation

This document is organized and requirements are allocated as shown in the following table:

| MORD Section | Requirements | Allocated to: | Requirements Accepted By: |
| --- | --- | --- | --- |
| 1 | Introduction | All Elements | All |
| 2 | Mission Level Requirements | All Elements | All |
| 3 | Ground Station Requirements | GSFC, Code 450 | Bob Stelmaszek |
| 4 | Ground Communications | GSFC, Code 423 | Clayton Sigman |
| 5 | Mission Operations Center | Ball Aerospace | Richard Cassell |
| 6 | Flight Dynamics System | Ball Aerospace | Scott Mitchell |
| 7 | Instrument Support Facility | Science Team | Peggy Jester |
| 8 | Level Zero Data Processing | GSFC, Code 423 | Timothy Rykowski |
| 9 | Science Data Processing | GSFC, Code 971 | David Hancock |
| 10 | Science Data Archival & Distribution | GSFC, Code 423 | Stan Scott |
| 11 | Spacecraft Contractor Requirements | Ball Aerospace | Richard Cassell |
| 12 | GLAS Instrument Developer Requirements | GSFC, Code 924 | James Abshire |
| 13 | Science Team Requirements | Science Team | Bob Schutz |

## Applicable Documents

The following are applicable documents to the MORD:

- ICESat Mission Systems Requirements Document, 2/98.

- Ground System Interface Control Document; Data, 12/10/98.

- Ground System Interface Control Document; Radio Frequency, 4/99,

- Operations Handbook for the ICESat Observatory.

- EOSDIS Architecture Description Document (latest version on WWW).

- GLAS Instrument Description Document

- GLAS I-SIPS Software Architectural Design Document, October, 1998 (Version 2.0)

- GLAS Science Computing Facility (SCF) Plan, February, 1998 (Version 0.4)

# Mission Level Requirements

## Mission Phases

The following flow chart describes the major ICESat Mission Phases that shall be supported.

A description of each mission phase follows:

- Development Phase – the development and fabrication phases of each key mission element (GLAS, BUS, IGS, and SCF/SIPS)

- Integration & Test Phase – the I&T of each of the major mission elements as stand-alone elements, followed by a series of integration and test between the various mission elements.  This phase culminates in a series of ICESat System End-to-End Check-out tests, including end-to-end data flow tests, simulations, and dress rehearsals.

- Launch Phase – these are all activities from packaging and shipment of the Observatory through launch and orbit insertion of the Observatory.

- Spacecraft Bus Check-out Phase – this is the time period from launch through acceptance of the spacecraft Observatory from Ball Aerospace by the government.  This phase includes the activation and check-out of the spacecraft’s subsystems.  This phase is expected to last ~ L + 30 days.

- Instrument Check-out phase – this phase coincides with the Spacecraft Bus Check-Out Phase and includes activation and check-out of the GLAS instrument’s subsystems.  This phase begins ~ L + 5 days, immediately after key Spacecraft Bus subsystems have been activated.

- Transition to Operations Phase – this phase also coincides with the Spacecraft and Instrument Check-out Phases and culminates with transitioning flight operations control from the spacecraft contractor to the flight operations team ~ L + 30 days.

- Calibration & Validation Phase – this phase covers the time period from ~ L + 30 days to ~ L+ 120 days and includes the calibration and validation of the GLAS instrument’s subsystems and measurements.

- Nominal  Science Phase – this is the operations phase of the ICESat mission beginning ~ L + 120 days.  Normal operations includes activities such as orbit determination and maneuver planning/execution.  Contingency operations includes operational responses to any anomalies that may occur.  Mission maintenance includes any modification to GLAS or BUS flight software and any systems maintenance that may occur on the ground.

- NOTE:  In addition, mission maintenance includes a periodic return (expected ~ L + 3 years) to the Calibration & Validation Phase resulting from the expected transition to back-up GLAS lasers due to expected laser deterioration.

- Platform Disposal Phase – this phases begins when the Observatory’s expendable resources have been depleted  (L +  5 years).  Note that the ICESat space segment has been designed for 3 years of operations with a goal of 5 years.  Analysis indicates that the Observatory is expected to naturally reenter the earth’s atmosphere 25 years after EOL (~ L + 30 years).

## Mission Data Flow

The following architecture diagram defines the top-level data flow to be supported by each of the ground system elements.

## Mission Operations Documentation

Mission operations documentation is defined as those documents that are required to define, build, test, operate, and maintain the ICESat ground systems.  The following table lists key documents and other media-based deliverables that are critical to the ICESat mission operations development.  Some names and contents of documents are expected to change based on each element’s unique documentation system currently in place and these will be negotiated and documented as an update to this document.  However, the intent, as is evident by the title of each document, shall be retained.

| IGS Doc # | Document Title | Source | Actual DOC # | Comments/Trace |
| --- | --- | --- | --- | --- |
| 2.01 | IGS Master Schedule | All |  | IGS Requirement |
| 2.02 | IGS Test Plan | TBD |  | Overall Test Plan for all IGS elements |
| 2.03 | Mission System Requirements Document for ICESat Mission | Project |  |  |
| 2.04 | Mission Operations Requirements Document (MORD) for ICESat, Versiom 1.0 | Project | ICES-401-SPEC-002 |  |
| 2.05 | Observatory Launch Site Operations and Test Plan | Ball |  | RSA CDRL 11 |
| 2.06 | Spacecraft Observatory Integration and Test Plan | Ball |  | RSA CDRL 6 |
| 2.07 | GLAS Instrument Laser Safety Analysis 11/1/98 | 924 | GLAS-924-ANYS-001 |  |
| 2.08 | Environmental Assessment | Project |  |  |
| 2.09 | ICESat Mission Operations Concept Document | Project |  |  |
| 2.10 | Project Support Level Agreement (PSLA) | Project |  |  |
| 2.11 | MOC/FOT/FDS Procurement Package to SOMO/CSOC | Project |  | MOC requirements to SOMO |
| 3.01 | Ground System Interface Control Document; Data | Ball |  | RSA CDRL 5B, See ICD # 1 in IGS Architecture |
| 3.02 | RF ICD between the ICESat Spacecraft and the EPGS | Ball |  | RSA CDRL 5A, See ICD # 1 in IGS Architecture |
| 3.03 | Network Operations Support Plan for the ICESat Mission | 450 |  | Similar approach used for QuikSCAT doc |
| 3.04 | IGS CTV Support Plan | 450 |  | Similar approach used for QuikSCAT |
| 3.05 | EPGS IGS Design Spec & Ops Plan | 450 |  |  |
| 3.06 | EPGS/WFF Test Plan | 450 |  |  |
| 4.01 | IGS Security Plan | 423 |  |  |
| 4.02 | IGS Ebnet/NISN ICDs | 423 |  |  |
| 4.03 | Ebnet/NISN Test Plan | 423 |  |  |
| 5.01 | ICESat T&C Handbook | Ball |  | RSA CDRL 5A |
| 5.02 | Spacecrat Operations Description Manual for the ICESat Observatory | Ball |  | RSA CDRL 8 |
| 5.03 | Mission Requirements Document | Ball |  | RSA CDRL 18 (Mission requirements document for the spacecraft & ground system |
| 5.04 | Spacecraft Operations Handbook for the ICESat Observatory | Ball |  | RSA CDRL 10 |
| 5.05 | MOC External Interfaces ICD | LASP |  | Similar approach used for QuikScat MOC ICD. See ICD # 9 in IGS Architecture |
| 5.06 | Detailed MOC Requirements & Design Document | LASP |  | Include MOC Design, Staffing &Training Plans, Facility Plans |
| 5.07 | MOC Operations Concept Document (MOCD) | LASP |  |  |
| 5.08 | MOC Flight Operations Procedures | LASP |  | Detailed Operations Procedures and Contingencies |
| 5.09 | MOC Operational Agreements with FDS, IOT, ST, and other mission elements (EPGS, WFF, etc.). | LASP |  |  |
| 5.10 | EDOS to DAAC ICD (DELETED) | N/A | Deleted | See ICD # 3 in IGS Architecture |
| 5.10 | MOC Test Plan | LASP |  |  |
| 5.11 | Spacecraft Database (Electronic) | Ball |  |  |
| 6.01 | FDS Detailed Requirements and Design Specification. | FDS |  | FDS design, staffing, facilities, etc. |
| 6.02 | FDS Operations Procedures Handbook. | FDS |  |  |
| 6.03 | FDS Test Plan (FDSTP). | FDS |  |  |
| 6.04 | FDS Operational Agreements with FOT, IOT, ST, and other mission elements (EPGS, WFF, etc.). | FDS |  |  |
| 6.05 | Flight Dynamics External Interfaces ICD | TBD |  | Serves as response to MORD. See ICD # 7 in IGS Architecture |
| 7.10 | GLAS Instrument Support Facility (GISF) External Interfaces ICD | ISF |  | See ICD # 8 in IGS Architecture |
| 7.20 | GLAS Operations Agreements | ISF |  |  |
| 7.30 | GLAS Database (Electronic | GSEF |  | GLAS Database for MOC |
| 8.01 | ICD Between EDOS and EGS Elements (Appendix to address ICESat Specifics) | EDOS |  | See ICD #2. This is EDOS CDRL B301. Replaces 5.10 and 9.01 |
| 8.02 | EDOS Detailed Design Specification | EDOS |  |  |
| 8.03 | EDOS Test Plan | EDOS |  |  |
| 9.01 | SCF to GSFC DAAC ICD (DELETED) | N/A | Deleted | See ICD # 4 in IGS Architecture |
| 9.02 | GLAS ISIPS ICD (Appendix to existing generic ISIPS ICD) | SCF |  | See ICD # 5 in IGS Architecture |
| 9.03 | GLAS ISIPS Softward Architecture Design Document | SCF |  |  |
| 9.04 | ICD between ISIPS/IST and CSR | SCF |  | See ICD # 6 in IGS Architecture. Internal ICD to ISIPS/SCF. |
| 9.05 | GLAS Level 0 Instrument Data Product Specification Ver 2.2 | SCF |  |  |
| 9.06 | GLAS Level 0 Instrument Data Products Specification Level 1 Ver 1.2 | SCF |  |  |
| 9.07 | GLAS Standard Data Products Specification Level 2 Ver 1.2 | SCF |  |  |
| 10.01 | DAAC Design Document | DAAC |  |  |
| 10.02 | DAAC Test Plan | DAAC |  |  |
| 10.03 | User Guide for GLAS Data (Describes how users access GLAS data from NSIDS | NSIDC |  |  |
| 11.01 | Spacecraft Engineering Data Archive | Ball |  |  |
| 11.02 | Spacecraft Sustaining Engineering Support Plan | Ball |  |  |
| 11.03 | Spacecraft Flight Software Maintenance Support Plan | Ball |  |  |
| 11.03 | Spacecraft Simulator User's Manual | Ball |  |  |
| 11.04 | Spacecraft Activation, Check-Out, and Transition Plan | Ball |  |  |
| 11.05 | Spacecraft FMECA Analysis | Ball |  |  |
| 12.01 | GLAS Engineering Data Archive | 924 |  |  |
| 12.02 | GLAS Sustaining Engineering Support Plan | 924 |  |  |
| 12.03 | GLAS Flight Software Maintenance Support Plan | 924 |  |  |
| 12.04 | GLAS Operations Manual | 924 |  |  |
| 12.05 | GLAS Fligth Software Manual | 924 |  |  |
| 12.06 | GLAS Training Plan & Materials | 924 |  |  |
| 12.07 | GLAS FMECA Analysis | 924 |  |  |
| 13.01 | GLAS Calibration & Validation Plan | ST |  |  |

## Major Reviews

The following are key operations and ground system reviews that shall be supported.

| Review Name | Description & Relationship to Mission Operations and Ground Systems | Lead Element | Month/Year |
| --- | --- | --- | --- |
| IGS Critical Design Review | Overall Design Review of all Ground System elements (MOC, FOT, IOC, IOT, FDS, etc.). | BASD | December, 1999 |
| Mission Operations Review (MOR) | Demonstration of mission operations readiness to support mission, including I&T support. Joint review with BASD, GLAS, ESDIS, CSOC, and Science. | BASD | December, 1999 |
| Flight Operations Review | Demonstrate that all flight and ground systems and personnel reflect the deployed state of the system. Joint review with BASD, GLAS, ESDIS, CSOC, and Science. | BASD | April-01 |
| Operations Readiness Review (ORR) | Focuses on networks support readiness for ICESat. Also supported by MOC, ESDIS, etc. | CSOC | May-99 |
| Launch Readiness Review (LRR) | (also called FRR) Demonstrates readiness to launch the spacecraft by all mission elements. Joint review with BASD, GLAS, ESDIS, and Science. | BASD | June-01 |
| Mission Activation Review | Review by all mission elements of successful activation, transition, and calibration events. | ICESat Project | August-01 |

## Mission Operations Development Support

Each mission element shall support the definition, implementation, testing, and transition to operations of the ICESat   This includes participation in working groups and planning sessions, preparing materials, and participating in activities such as working sessions, reviews, testing, status reporting, simulations, and dress rehearsals.

## Acceptance and Transition Roles and Responsibilities

- From the time of launch to final spacecraft acceptance by the government, the BASD Flight Director shall bear full responsibility, in concert with a team of experts from NASA, Ball, and the Instrument Developer, for the health and safety of the ICESat Observatory.

- After acceptance by the government, the BASD, through the MOC/FOT organization  shall have full responsibility for the health and safety of the ICESat Observatory for the life of the mission.

# EOS Polar Ground Stations

The EPGS Project consists of three ground stations: Alaska Ground Station (AGS), Svalbard Ground Station (SGS), and Wallops Ground Station (WGS).  These ground stations shall provide space-ground telecommunications services for the ICESat spacecraft.  These services consist of S-band command, S-band telemetry, and X-band telemetry.   The Ground Network Project Office shall provide the use of the EOS Polar Ground Stations in Alaska (AGS) and Norway (SGS) for the life of the mission.  The Ground Network Project Office shall also provide the use of WGS for back-up S-band command and telemetry support, including contacts to confirm certain periodic maneuvers that occur over the equator on the ascending pass towards Wallops.  Code 450 shall provide the use of the EOS Polar Ground Stations in Alaska (AGS) and Norway (NGS) for the life of the mission.  The contact schedule is described in the next section.

## Interface Standards

- Up-link and down-link  data formats are CCSDS compatible and data interface standards adhere to Applicable Document #2.

- Radio frequency interface specifications are specified to be compatible with the EOS Polar Ground Stations, as stated in the Applicable Document #3.

- The EPGS technical experts or their designees shall participate in the development and maintenance of these ICDs.

## Baseline Ground Station Contact Scenario

The EPGS shall support the following ground station contact scenario.

| Contact Characteristics | X-band Down @ 40 Mbps | S-Band Down @ 264 Kbps | R/T S-band Down @ 16 Kbps | S-band Up @ 2 Kbps |
| --- | --- | --- | --- | --- |
| Base-line ground station antenna elevation angle for AOS | 10 degrees | 5 degrees | 5 degrees | 5 degrees |
| Minimum Link Margin guaranteed by ICESat project at 10 degrees. | 3dB | > = 3dB | 3dB | > = 3dB |
| Minimum Scheduled Contacts from Launch Through Calibration L + 120 days | Up to one contact every orbit | Up to one contact every orbit. | Up to one contact every available pass. | Up to one contact every available pass. |
| Minimum Scheduled Contacts for post-calibration normal operations from L+120 days to EOL | At least one contact every 6 hours | At least one contact every 6 hours | At least one contact every 6 hours | At least one contact every 6 hours |
| Contact Duration | Which ever comes first: time to dump SSR or time when contact terminates. | Which ever comes first: time to dump DSU or time when contact terminates. | Which ever comes first: time to dump DSU or time when contact terminates. | Which ever comes first: time to dump DSU or time when contact terminates. |

After launch, the ground stations shall characterize the X-band communications links and determine a baseline contact scenario.  This contact scenario will define the minimum ground antenna elevation angle for acquisition of signal (AOS).  The baseline elevation angle for AOS is currently 10 degrees.

## Emergency Commanding

Emergency commanding shall be made available within one orbit after the declaration of a flight system emergency by the flight operations team.

## Wallops Flight Facility Ground Network Scheduling System

The Wallops Orbital Tracking Information System (WOTIS), located at the Wallops Flight Facility (WFF) is the central facility that the ICESat Mission Operations Center (MOC) interfaces with for scheduling ground station resources and obtaining post-pass reports.  WOTIS will ingest the ICESat project schedule requests, employ de-confliction algorithms, and distribute the final schedules to ground stations and the ICESat MOC.  WOTIS will provide scheduling support 24 hours per day, 7 days a week.  Table 3-1 lists the typical transactions and transaction timing between the ICESat MOC and WOTIS.

Table 3-1. Typical WOTIS File Interchange Timeline

| Step | File & Content | Action | Time Period |
| --- | --- | --- | --- |
| 1 | Strawman Schedule Contains initial supports at all GS using resources per the ICD | WOTIS generates initial schedule, using WOTIS generated Inviews, according to WOTIS/ICESat agreed scheduling rules. | T-3 weeks |
| 2 | Update to Strawman Schedule Contains only those supports needed by ICESat | MOC returns schedule to WOTIS with those supports needed, and may adjust times and activity codes; a new support may be requested, if needed. If Strawman is correct, no update needs to be returned. | T-3,2 weeks |
| 3 | Operations Schedule Contains supports as they will be processed at each GS | WOTIS sends final Operations schedule to MOC, if desired. | T-1 week, usually Tuesday before Ops week |
| 4 | Ephemeris | MOC sends IIRV or corrected NORAD 2-Line Elements, if needed; otherwise WOTIS automatically gets orbital elements from the Internet. | At least 3 days before pass to accommodate weekend and holiday operation. New data overwrites old data. |
| 5 | GS Operations Schedule (AOTS Master) | WOTIS generates weekly and/or daily Operations Schedule (containing ephemeris) and forwards to GS via FTP. | Time span is for Operations week, generated on Thursday/Friday & updated daily as needed |
| 6 | Post-Pass Summary File Contains the summary statistics from the support | WOTIS provides a summary of support results to MOC shortly after the completion of the support. | After each pass |

.

## McMurdo Ground Station Support

The McMurdo Ground Station (MGS) shall be available as a non-launch critical back-up resource for S-band RT and Playback telemetry and commanding of the ICESat Observatory.  Under no circumstances shall ICESat be used as a driver for any development costs incurred by MGS.  MGS is to be utilized only if available.

## Doppler Ranging

The ground stations (AGS and, SGS, and WGS) shall provide two-way Doppler data for launch and early orbit check-out of the ICESat spacecraft, and for contingency operations in the event of on-board Global Positioning System (GPS) receiver failure.

## S-band Command & Telemetry Command Processing

- All ground stations (AGS, SGS, and WGS) shall provide received Real-Time S-band telemetry data to the Mission Operations Center (MOC).

- All ground stations shall transmit commands received from the MOC to the ICESat spacecraft.

- All ground stations shall forward received S-band Playback telemetry data and all Real-Time S-band telemetry data to EDOS.

- AGS and SGS shall forward all received X-band data to the EDOS Ground Station Interface Facility (GSIF)

Spacecraft Raw Data Latency:  The following data shall be made available for use by the FDS.:
a. X-band data packets that contain GPS raw data shall be available via EDOS at the FDS no later than 6 hours after the X-band ground station contact is completed.
b. S-band real-time data, including GPS on-board solutions data, shall be available at the FDS within 1 minute of ground station contact.
c. S-band playback data shall be available at the FDS via EDOS within 30 minutes of ground

## Compatibility Test Van Support

- The Compatibility Test Van (CTV) shall be made available at the spacecraft contractor’s I&T facility for Radio Frequency testing of the ICESat spacecraft at the designated X-band and S-band frequencies.

- CTV Test Plans and Procedures, including facility and communications requirements, shall be provided.

- A CTV Test Report shall also be provided.

- The CTV shall also test at the WGS for compatibility, as required.

## Communications Links Testing

Provisions shall be made such that the ground stations shall accept X-band and S-band test data as recorded from the spacecraft on CD-ROM media or direct transmission through commercial T-1 rate data links.  This data shall be modulated and transmitted through the ground stations (only S-band for WGS) for simulated playback through the ground system.

# Ground Communications

The ESDIS Project shall provide all ground communications infrastructure to support the mission requirements.

## Mission Operations System Communications

ESDIS shall provide all ground communications networks and links required to support the ICESat mission operations, including long-haul data services from the polar ground stations to GSFC and inter-system communications that provide communications between all ground system elements and the Control Center, including voice loops, data lines, fax lines, and Internet connections.

## Spacecraft Integration & Test Communications

ESDIS shall provide a data communications link between the spacecraft facility, Boulder, CO, and the EOC to be used for commanding and receiving telemetry from the spacecraft.  The communications link shall be sized to support the S-band telemetry and command channels to/from the spacecraft.

## Launch Pad Communications

ESDIS shall provide data communications link between the launch pad and the EOS Operations Center used for final check-out of the spacecraft and instrument prior to launch.  The communications link shall be sized to support the S-band telemetry and command channels to/from the spacecraft.

## TDRS Communications

TDRS communications services are not required for the ICESat mission, nor is it practical to close the Radio Frequency (RF) link due to low link margins.

## Science Distribution Communications

ESDIS shall provide all network support services required to interconnect the data archive centers and the Science Computing Facilities.  Specifically, support the exchange of processed science data from the SIPS to the NSIDC DAAC and ESDIS shall provide all external network connectivity to distribute science data products to the end user.

## Communications Testing

ESDIS shall test and verify all communications links prior to interfacing with any ICESat mission element, the purpose of which is to mitigate risks due to unknown interface performance.

# Mission Operations Center

## Mission Communications Support Profile

The following chart shows the expected number of contacts expected to be supported by the MOC/FOT for the major mission phases shown.

| Contact Characteristics | X-band Down @ 40 Mbps | S-Band Down @ 264 Kbps | S-band Up @ 2 Kbps | R/T S-band @ 16 Kbps |
| --- | --- | --- | --- | --- |
| Minimum Scheduled Contacts from Launch Through Calibration L + 120 days | Up to one contact every orbit | Up to one contact every orbit. | Up to one contact every available pass. | Up to one contact every available pass. |
| Minimum Scheduled Contacts for post-calibration normal operations L+ 120 days to EOL | At least one contact every 6 hours | At least one contact every 6 hours | At least one contact every 6 hours | At least one contact every 6 hours |

## Major Interfaces

The MOC shall interface with other elements of the ICESat Ground System.  Refer to the data flow diagram on the following page.

A description of each external interface element is provided below.

- EOS Polar Ground Station (EPGS) in Alaska and Norway – EPGS’s are the primary ground stations for S-band command and telemetry and X-band data communications with the ICESat Observatory.  The MOC shall interface with EPGS for real-time (R/T) housekeeping data and for command uploads.

- Wallops Ground Station (WGS) in Virginia – WGS provides back-up S-band command and telemetry interfaces.  The MOC shall interface with WGS for backup command and control interfaces.

- Wallops Orbital Tracking Information System (WOTIS) in Virginia – the WOTIS provides planning and scheduling of ground station resources.  The MOC shall interface with WOTIS to coordinate scheduling of the ground system.

- Earth Observing System (EOS) Data and Operations System (EDOS) at GSFC – EDOS provides the processing of Playback (PB) S-band housekeeping data and recorded X-band science data.  The MOC shall interface with EDOS for receipt of the processed S-band data and for the exchange of scheduling information.

- GSFC Flight Dynamics System (GFDS) at GSFC – GFDS will primarily provide support during launch and early orbit (L&EO) and shall provide processing of the launch vehicle’s separation vector and provide acquisition data to the EPGS.  The MOC shall interface with the GFDS and receive these GFDS products for command generation to adjust the Observatory’s orbit and attitude.  GFDS may also be called upon to support emergency situations.

- EOSDIS Backbone Network (EBnet) and NASA Integrated Support Network (NISN) – Ebnet and NISN provide all communications networks that provide connectivity to all ground system elements.  The MOC shall utilize these networks for all communications requirements external to the MOC.

- Instrument Support Facility (ISF) at GSFC – The ISF conducts long term instrument trending and analysis and contains the Instrument Operations Team (IOT).  The MOC shall interface with the IST and receive science planning products and command requests generated by the IOT.

- ICESat Integration & Test (I&T) Facility at Ball Aerospace – The MOC shall  interface with the Ball I&T facility during all phases of the I&T process.  The I&T facility will also contain the Spacecraft Bus Simulator (SBS) to be used by the MOC when the spacecraft is not available for testing.

- ICESat Sustaining Engineering Facility (ISEF) at Ball Aerospace – The ISEF will contain the ICESat Flight Software Test Bed (FSTB).  The MOC shall interface with the FSTB after launch to support testing of any software modifications and to receive software uploads generated by the FSTB.  The ISEF includes personnel with which the MOC shall interface for anomaly resolution and trending analysis.

Blank Page.

## Flight Systems

- The contractor shall provide all MOC hardware and software systems.

- Only off-the-shelf or reusable control center software shall be proposed.  No custom control center software solutions shall be proposed, except for unique scripts to code routine operations and monitoring, trending analysis, calculations, or display formats that may be necessary to meet unique requirements.

## Facility

- The contractor shall provide all facilities necessary to house the systems and personnel that comprise the MOC, including floor space, Heating, Ventilation, and Cooling (HVAC), lighting, and physical security.

- Office space with a desk and internet connection for up to four project personnel (such as instrument engineers, project staff, etc.) shall be provided.

## Operational Coverage

- The MOC shall operate on a basis consistent with the mission’s science requirements, schedule, and ground station contact scenarios.  Autonomous (“lights out” or “brown out”) operations are encouraged as a means of reducing mission costs.

- All hardware and software systems shall operate on a 24 hour per day basis, 365 days per year.

- ICESat operations shall be conducted in coordination with the ICESat science objectives and plans as generated by the IOT and the science team (ST).

## Database Compatibility

The MOC software shall be compatible with the Operations and Science Instrument Support (OASIS) database format.  All ground systems to be implemented shall be compatible with the OASIS database and be driven by Integration & Test (I&T) database electronic files provided by Ball Aerospace.

## Planning and Scheduling

- The MOC shall coordinate the planning and scheduling of all ground system resources and contacts.

- The MOC shall provide for the planning and scheduling of all flight related activities, including interfacing with the Instrument Operations Team for science maneuver planning.

- The MOC shall integrate the experiment command requests from the IOT.

- The MOC shall produce the spacecraft’s operation schedule and operations timelines.

## Real-time Observatory Telemetry Monitoring

- The MOC shall monitor all real-time flight critical telemetry during all ground station contacts.

## Trending Analysis

- The MOC shall conduct long term trending and analysis of the ICESat Observatory’s playback telemetry collected over the life of the mission.  This includes critical spacecraft bus and instrument telemetry.

- The MOC shall provide predicted trends for critical Observatory parameters.

- The MOC shall deliver monthly trending curves and data reports shall be provided to Ball Aerospace for analysis and long term performance assessment.

## Observatory Commanding

- The MOC shall provide for the real-time commanding of the ICESat Observatory.

- The MOC shall provide for the generation of stored command strings to be up-linked to the ICESat Observatory.

- The MOC shall provide the uploading of parameters (such as tables, software, etc.).

## Remote Monitoring Terminal

- A monitor-only remote MOC terminal shall be provided to the ISF/IOT to support the monitoring of the ICESat Observatory by the IOT during all phases of the mission.

- Four monitor-only MOC terminals located at the MOC for use during launch and early orbit check-out operations by instrument and spacecraft bus engineering personnel shall be provided.  These terminals shall be retained for the life of the mission.

## Sustaining Engineering

The contractor shall maintain the MOC and perform sustaining engineering of all MOC hardware and software systems.  This shall include the loading and testing of any software upgrades, hardware upgrades, and facility improvements required to sustain operations for the life of the ICESat Observatory.

## Anomaly Resolution

- The MOC shall provide support for anomaly resolution of all Observatory anomalies.  This includes coordinating such efforts with subsystem experts from Ball Aerospace and the GLAS instrument developer.

- Anomaly resolution includes interfacing with the GLAS developer and Ball Aerospace for the maintenance, correction, and uploading of flight software and other uploadable parameters.

- Monthly Anomaly reports shall be provided to the GSFC Reliability and Safety Office.

## MOC Data Archive

- The MOC shall receive and permanently archive all S-band real-time and playback telemetry for the life of the mission.

- The MOC shall archive and make available to authorized users via File Transfer Protocol (or similar Internet connection) all products generated by the MOC, such as command files, maneuver planning files, trending data, schedules, etc.  These files shall be maintained for the life of the mission.

- The MOC shall archive and make available to authorized users via File Transfer Protocol (or similar Internet connection) all products received by the MOC, such as maneuver planning products and orbit determination solutions received from the FDS.  These files shall be maintained for the life of the mission

## Laser Flight Safety Operations

There are no laser flight safety operational requirements for ICESat.

## Flight Operations Team

### Staffing and Organization

The contractor shall provide a flight team organization chart that at a minimum consists of a Flight Director and a FOT.  A description of the roles and responsibilities of the Flight Director and each FOT member shall be provided.

### Personnel Availability

- The contractor shall provide a dedicated Flight Director and at least one dedicated FOT member to support the development of the ICESat MOC/FOT.  These individuals shall be referenced by name and shall be available to support the MOC/FOT development during all phases of the pre-launch period.  The FD or a lead FOT member shall be made available to support MOC/FOT development upon contract award.

- These named individuals shall coordinate all activities directly with the ICESat Project’s Operations Manager.

### Emergency and Anomaly Access

The contractor shall provide a system whereby members of the FOT shall be available on an on-call basis to provide anomaly resolution support in the event that a spacecraft emergency or anomaly situation occurs.

### Training and Certification

Pre-launch training and post-launch continued training of the FOT personnel, including continued certification in flight operations of the ICESat Observatory shall be provided.

### Rehearsal Support

The contractor shall support at least 3 Flight Operations Rehearsals for the purpose of training and developing flight operations proficiency.  Each Rehearsal shall nominally be scheduled for a 5 day period at 24 hours each day.  The Rehearsals to be supported are outlined as follows:

| Rehearsal # | Purpose | Rehearsal Need Dates |
| --- | --- | --- |
| Rehearsal # 1 | Basic Operations Training | L – 3 months |
| Rehearsal # 2 | Anomaly resolution and trouble-shooting. | L – 2 months |
| Rehearsal # 3 | Full Flight Dress Rehearsal | L – 2 months |

## Reliability

- The MOC shall be designed for an availability that meets the operational coverage requirements set forth in this MOPS.  The contractor shall propose an availability calculation, along with supporting rationale, for the MOC/FOT system.

- No single point hardware or software failure points shall be implemented in the Real-Time telemetry and command processing system.

- Maintenance shall be scheduled during non-contact times and shall be conducted on only a non-operational functional string to ensure that a functioning string is always available to support telemetry monitoring and commanding.

## Security

- Physical security shall be provided and demonstrated such that the MOC facility and systems shall be secured from unauthorized access.  Unrestricted access to MOC facilities and computer systems is not acceptable.

- The MOC’s computer systems and supporting network interfaces shall be protected from unauthorized access.

- Flight Database access and updates shall be controlled.

- Security measure shall be taken to prevent database corruption and permanent database loss.  At a minimum, a backup copy of all changed software, databases, and documentation shall be retained in a separate physical location other than the MOC.

## Observatory Integration and Testing Support

The MOC/FOT shall interface with Ball Aerospace during all phases of the Observatory  I&T process.  This includes participating in all ground system simulations and rehearsals, including end-to-end science data flow tests, and interfacing with the Spacecraft Simulator and the Flight Software Test Bed (FSTB).  The FSTB is the flight software development environment used by Ball Aerospace for the development, testing, and maintenance of flight software.  In addition, the FSTB is used to simulate a high fidelity attitude control system.

In addition, the contractor shall interface with the Spacecraft Ground Support Equipment (GSE) to support integration & test activities.  The contractor is encouraged to perform a site visit to fully understand these interface requirements.

## Documentation

The contractor shall deliver the following documents to NASA/GSFC.  If existing documentation structures used on other missions currently exist, these may be used in lieu of these documents provided they contain the necessary information.

Mission Operations Center Documentation:

- Integrated MOC/FOT/FDS Development Schedule.

- MOC External Interfaces Control Document (MEICD) that includes interfaces between all external MOC interfaces.

- Detailed MOC Requirements & Design Document (DMR&DD), that includes derived requirements, detailed design, staffing & training plans and facility plans.

- MOC Test Plan.

- MOC Flight Operations Procedures (MFOP).

- Operational Agreements with IOT, ST, and other major ground system elements (EPGS, WFF, EDOS, etc.).

Flight Dynamics Documentation:

The FDS contractor provide the following documentation:

- FDS External Interface Control Document (FEICD) (may be combined with the MOC External Interfaces ICD).

- FDS Detailed Requirements and Specification.

- FDS Test Plan (FDSTP).

- FDS Operations Procedures Handbook.

- Operational Agreements with the FOT, IOT, ST, and other mission elements (EPGS, WFF, etc.).

## Reviews and Status Reporting

The contractor shall provide the following reviews and status reporting (note, some reviews likely to be combined with existing reviews base-lined in the ICESat contract):

- Status Reports to the ICESat Operations Manager (Monthly)

- Requirements/Design Review (~  L - 18 months)

- Flight Operations Review (~L - 4 months)

- Launch Readiness Review (~L - 1 months)

- The contractor shall provide a FDS Design Review (FDSDR) subject to a peer review approval of the design by a peer review team made up of the Goddard Space Flight Center’s Flight Guidance and Navigation personnel, Science Team  personnel, and University of Colorado personnel.

# Flight Dynamics System

The Flight Dynamics System (FDS) shall be that part of the MOC which provides overall Guidance & Navigation (G&N) for the ICESat mission.  With the exception of the  NASA-provided services described below, the contractor shall provide all the FDS functions described in Section 4.

NASA Provided Flight Dynamics Services

There are flight dynamics related services that will be provided by the GSFC Flight Dynamics (GFD) Guidance & Navigation Branch that will support the contractor provided FDS and will include the launch and early orbit (L&EO) support traditionally provided by GFD for other satellite projects.  The GFDS will interface with the contractor provided FDS for this L&EO support.

The following L&EO functions will be provided by the GFD:

- Work with NASA ground stations to analyze and verify tracking system accuracy.

- Serve as the interface to the launch contractor for acquiring and processing launch trajectory  predicts and initial post-separation spacecraft orbit predicts.

- Acquire LTAS data from launch site and process to generate initial orbit predict.

- Acquire NORAD tracking data and process to generate orbit predicts.

- Acquire UTDF angles tracking data from NASA ground stations after passes and process into orbit predicts.

- Generate initial orbit predict after spacecraft separation and distribute as IIRV to the MOC, WOTIS and to ground stations.

- Generate updated orbit predicts every four hours for the first 24 hours after launch and distribute as IIRVs to the MOC, WOTIS and ground stations.

- Generate updated orbit predicts every 24 hours, starting one day after launch and continuing through seven days after launch and distribute as IIRVs to the MOC and WOTIS.

- Orbit Determination based on Ground Station Doppler-ranging and X-Y angles data from the ground tracking stations (if GPS data is not available).

NOTE:  The contractor shall provide all FDS functions described in the remaining sections of Section 4.

## Mission Characteristics

The following are the top-level ICESat mission characteristics applicable to the FDS.

- Inclination = 94 degrees.

- Altitude = 600 km.

- Orbit = non-sun synchronous frozen orbit.

- 2 repeat orbits (183 days during mission and 8 days during calibration).

- +/- 800 meter ground track control at all latitudes.

- Spacecraft Raw Data Latency:  The following data shall be made available for use by the FDS.

- X-band data packets that contain GPS raw data shall be available via EDOS at the FDS no later than 6 hours after the X-band ground station contact is completed.

- S-band real-time data, including GPS on-board solutions data, shall be available via the EPGS and WFF at the FDS within 1 minute of ground station contact.

- S-band playback data shall be available at the FDS via EDOS within 30 minutes of ground station contact.

## Software, Hardware, Personnel, and Facilities

- The contractor shall provide all FDS software development and maintenance and all hardware systems and training required to operate the software for the life of the mission.

- The contractor shall provide all FDS personnel and facilities required to operate the flight dynamics systems for the life of the mission.

## Mission Phases Support

### Maneuver Constraints

- No maintenance maneuvers shall occur over Antarctica or at points above 60 degrees latitude that are coincident with Greenland over-flights except in special or emergency circumstances.

- Ground track maintenance shall be performed using only one maneuver when possible.

- Frozen orbit maintenance shall be done in conjunction with the ground track maintenance maneuver.

- Maneuvers shall be constrained to occur no more frequently than once daily to support the Precision Orbit Determination (POD).

### Pre-Launch Phase

The Pre-launch period shall cover all time up to separation from the launch vehicle.  The following FDS functions and services shall be provided:

- Mission Analysis and Design Delta Velocity (Delta V)  Budget calculation and analysis.

- Injection Orbit Selection analysis.

- Reentry analysis (lifetime).

- Ground Station coverage analysis.

- Launch window analysis.

- Operations Planning, including participation in launch rehearsals and simulations.

### Check-out Period Phase

The Check-out period is the time from launch vehicle separation to the time the spacecraft bus has been accepted by the government (approximately 30 days).  The following FDS functions and services shall be provided:

- Ingest and process launch vehicle separation vector from GFDS.

- Planning and calibration of all orbit raising maneuvers.

- Planning and calibration of all routine ground track maintenance maneuvers.

- Planning and calibration of inclination maneuvers.

- Thruster calibration for the orbit attainment maneuvers.

- Thruster calibrations for the orbit maintenance maneuvers.

- Orbit determination and prediction based on GPS data from the flight receiver.

- On-board attitude validation support.

- Anomaly resolution support.

- Sensor calibration support.

- Provide Orbit Predictions in Improved Inter-Range Vector (IIRV) format to the ground station network.

- Convert Maneuver Plan into commands and table uploads for uplink to spacecraft.

### Calibration and Validation Phase

The Calibration and Validation period covers all time from acceptance of the spacecraft by the government to the time that the GLAS instrument has been calibrated and validated and science data gathering begins.  The following FDS functions and services shall be provided:

- Planning and calibration of the inclination and ground-track maintenance  maneuvers.

- Support onboard orbit and attitude determination validation.

- Anomaly resolution support.

- Sensor calibration support.

- Generation of planning and scheduling data products used by the MOC.

- Provide Orbit Predictions in Improved Inter-Range Vector (IIRV) format to the ground station network.

- Convert Maneuver Plan into commands and table uploads for uplink to spacecraft.

### Maneuver Planning

The contractor shall provide maneuver planning and maneuver calibration for all phases of mission operations.  The FDS system shall be capable of designing three types of maneuvers:

- Drag Make-up Maneuvers - along track maneuvers to adjust the orbit semi-major axis shall be designed to change the ground-track drift rate relative to the exact repeat orbit.

- Inclination Maneuvers - across track maneuvers to adjust the orbit inclination shall be designed to change the ground-track offset at high latitudes relative to the exact repeat orbit.

- Orbit Change Maneuvers - two along track maneuvers to adjust the orbit semi-major axis shall be designed to switch between the calibration and mission orbits.

NOTE:  The effect of these maneuvers on the mean orbit elements and ground-track offset shall be predicted and communicated to the MOC.

### Ground-Track Monitoring and Prediction:

- The Ground-Track shall be monitored daily and compared to that of the calibration or mission orbit, whichever is appropriate. Such monitoring shall be valid for all latitudes.

- The Ground-Track evolution shall be predicted to aid in maneuver planning. Such predictions shall make use of solar activity predictions to anticipate atmospheric drag, and the effect of luni-solar gravity on the orbit inclination.

- The Ground-Track output shall consist of both a graphical display of predicted ground-track offset, and tables of predicted mean orbit element and ground-track offset evolution.

### Mission Planning Support

- Determine coarse real-time ICESat attitude.

- Provide mission planning aids.

- Provide attitude sensor hardware performance monitoring.

- Determine predictive ICESat  orbit ephemeris and perform maneuver prediction and planning.

- Provide near-real-time maneuver monitoring (temperature, pressure, etc.).

- Provide acquisition data products.

- Assess the post-maneuver spacecraft state.

## Orbit & Attitude Determination

### Operational Orbit Determination

The contractor shall provide Operational Orbit Determination (OOD) using GPS data from the flight receiver in combination with GPS data from a worldwide network of ground tracking sites. Accuracy and timeliness shall be as follows:

Orbit Monitoring and Maneuver Planning OOD:

- Along track position:  Within 5 meters (1 sigma).

- Across track position:  Within 5 meters (1 sigma).

- Radial position:  Within 1.0 meters (1 sigma).

- ODD Latency:  Within 2 hours after X-band data received at FDS.

- Comparison with POD:  Flight Dynamics shall compare the OOD with the POD generated by the ST on a periodic basis in support of the onboard GPS validation.

Propagation Accuracy of the OOD solution after 1 day:

- Along track position:  Within 1.0 kilometer (1 sigma).

- Across track position:  Within 10 meters (1 sigma).

- Radial position:  Within 10 meters (1 sigma).

- ODD Latency:  Within 2 hours after X-band data received at FDS.

Propagation accuracy of the OOD solution for Antenna Pointing ODD after 24 hours of propagation and 24 hours after a maneuver:

- Along track position:  Within 4 kilometers (1 sigma).

- Across track position:  Within 4 kilometers (1 sigma).

- Radial position:  Within 4 kilometers (1 sigma).

- ODD Latency:  Within 2 hours after X-band data received at FDS.

### Operational Attitude Support

The contractor shall provide the following Operational Attitude (OA) support:

- The FDS shall calculate and monitor off-nadir pointing by running the off-nadir pointing algorithm provided by the University of Colorado.

- The FDS shall generate the off-nadir quaternions and provide them to the MOC for uploading to the spacecraft.

## Sensor Support

The contractor shall provide for the operation, maintenance, and calibration of various sensors used on the spacecraft.

### Sensor Uploadable Parameters Support

The spacecraft contractor (Ball Aerospace) will provide periodic updates for the following sensors and subsystems.  FDS shall support these updates.

- Star Catalog for spacecraft bus star tracker:

- Updates with respect to proper stellar motion (estimated annual upload of approximately 50 stars).

- Updates of a star Precession Quaternion (estimated weekly upload).

- GPS Initial Conditions Vector - Initialization of the GPS receiver whenever a Spacecraft Control Computer (SCC) reset takes place.

- Magnetic Field Tables – Table upload approximately annually.

GSFC shall provide star tracker updates for the GLAS star tracker.

### Sensor Calibration Support

The contractor shall participate in the following calibration activities with support from the spacecraft contractor (Ball Aerospace) and science operations:

- Calibrate alignments of the Solid State Star Tracker (SSST), and Inertial Reference Units (IRU).

- Calibrate the star-tracker’s field-of-view (FOV) calibration coefficients.

- Calibrate the IRU scale factors and drift rate biases (3-axis calibration at varying rates).

## Products Exchange

### FDS Products to the Mission Operations Center

The contractor shall generate the following products for use by the MOC on a routine basis for all phases of the mission:

- Operational Orbit Determination and Propagated State Vectors.

- Maneuver Design (magnitude, attitude, and time).

- Ground Track Offset  Plot and Table (actual versus predicted time).

- Plots and Tables to monitor the frozen orbit, including Inclination, Eccentricity, and Argument of Perigee parameters.

- Initial Condition Vector for the SCC and/or GPS, as needed.

- Generation of base time load to correlate the spacecraft clock (clock correlation code).

- Orbit & Attitude verification support.

### MOC Products to the Flight Dynamics System

The MOC shall make available the following products to the FDS:

- Propulsion system data, including tank pressure and temperature.

- The MOC shall make available to the FDS by electronic file transfer all raw S-band real-time and playback data received and all products generated by the MOC.

- Solar Array Encoder Conversions.

Note:  The spacecraft contractor (Ball Aerospace) will provide the equations for the spacecraft mass model and the propulsion model.

### Flight Dynamics Products to the Science Team

The FDS shall make available the following products to the science team.

- Inertia & Mass Properties.

- Maneuver magnitudes and timelines.

- OOD solutions.

- CT-602 Star Tracker data.

### Data and Products Archive

The FDS shall maintain a data archive with the following characteristics:

- The FDS shall permanently archive all data received and products generated by FDS for the life of the mission.  In particular, all orbit elements and propulsion data shall be permanently archived.

- All data archives shall be readily accessible (via File Transfer Protocol, etc.) by authorized users external to the FDS for the life of the mission.

# Instrument Support Facility

## Instrument Flight Systems

All ISF hardware and software systems that are necessary to meet the instrument operations requirements shall be provided.

## Facility

- All facilities necessary to house the ISF systems and personnel that comprise the ISF shall be provided.  This includes floor space, lighting, and physical security.

- Office space with a desk and internet connection for up to two project personnel (such as an instrument engineer, project staff, etc.) shall be provided.

## Operational Coverage

- The ISF/IOT shall be operated on a nominal 5 day, 8 hour per day schedule.  Autonomous (lights out or brown) operations are encouraged as a means of reducing mission costs during non-normal working hours.

- All hardware and software systems shall operate on a 24 hour per day basis, 365 days per year.

## Planning and Scheduling

- The ISF/IOT shall generate science plans, goals and objectives, and schedules for instrument operations that are in accord with the science plans and objectives.

- The ISF/IOT shall generate any unique planning and scheduling, such as for off-pointing for specific geographic areas.

- The ISF/IOT shall generate all instrument command requests and transmit them to the MOC/FOT for transmission to the Observatory.

## Trending Analysis

- The ISF shall provide for the long term trending and analysis of the GLAS Instrument’s telemetry collected over the life of the mission.  This includes critical related spacecraft bus telemetry.

- Trending requirements shall be provided by the GLAS Instrument Developer.

- Monthly trending curves and data reports shall be provided to the GLAS Instrument Developer for analysis and long term performance assessment.

## Sustaining Engineering

The ISF/IOT shall provide for the maintenance of all ISF hardware and software systems.  This includes the loading and testing of any software upgrades, hardware upgrades, and facility improvements required to sustain operations for the life of the ICESat Observatory.

## Anomaly Resolution

- The ISF shall provide support for anomaly resolution of all Instrument anomalies and related spacecraft bus anomalies.

- The ISF shall interface with the GLAS Sustaining Engineering Facility (GSEF) and shall include interfacing with subsystem experts from the GLAS Instrument Developer.

- The GSEF shall include the GLAS Developer’s GLAS Software Maintenance Facility (GSMF) for the maintenance, correction, and uploading of instrument software and other uploadable parameters.  The ISF shall accept GLAS software uploads from the GSMF/GSEF for transmission to the MOC/FOT for transmission to the Observatory.

- Monthly Anomaly reports shall be provided to the GSFC Reliability and Safety Office.

## Instrument Operations Team

### Staffing and Organization

An Instrument Operations Team (IOT) shall be provided sufficient to meet the GLAS instrument’s operational requirements.  A staffing profile sufficient to meet the requirements of the ICESat mission shall be provided.  At a minimum, an IOT organization chart that consists of an Instrument Director and an IOT member shall be provided.

### Personnel Availability

- The ISF shall provide a dedicated Instrument Operations Director (IOD) and at least one dedicated IOT member to support the development of the ICESat IST/IOT.  These individuals shall be referenced by name and shall be available to support the IST/IOT development during all phases of the pre-launch period.

- The IOD shall coordinate all activities directly with the ICESat Project’s Operations Manager.

### Emergency and Anomaly Access

A system shall be provided whereby members of the IOT shall be available on an on call basis to provide anomaly resolution support in the event that a spacecraft or instrument emergency or anomaly situation occurs.

### Training and Certification

Pre-launch training and post-launch continued training of the IOT personnel, including continued certification in flight operations of the GLAS instrument and overall ICESat Observatory shall be provided.

# Level Zero Data Processing

Level Zero Data Processing (LZDP) shall be done on the X-band down-link data.

## General Level Zero Data Processing Functions

| 1.1 | EDOS shall provide a safe backup of all ICESat GLAS Level 0 data sets produced by EDOS. |
| --- | --- |
| 1.2 | EDOS shall support ICESat pre-launch activities (e.g., operational readiness tests and simulations). |
| 1.3 | EDOS shall maintain/assure the integrity of all ICESat data received, stored, and transmitted. |
| 1.4 | EDOS shall support ICESat operations 24 hours per day, 7 days per week on a continuous basis. |
| 1.5 | EDOS shall support the CCSDS AOS Grade of Service 2 and 3. |
| 1.6 | EDOS shall provide the capability for capture of all ICESat X-band high rate return link data on separate, non-volatile, physical media, and for storage for 30 days after receipt. |
| 1.7 | EDOS shall provide Reed-Solomon (Grade of Service II) decoding on the ICESat high rate return link data as required. |
| 1.8 | EDOS shall provide AOS CCSDS Path and Virtual Channel Data Unit services on ICESat return link data. |
| 1.9 | EDOS shall provide processing support to produce Level 0 data sets (production data sets) [PDSs] and expedited data sets [EDSs] for the GLAS instrument packets. |
| 1.10 | EDOS shall provide Customer Operations Data Accounting (CODA) reports to the ICESat Flight Operations Segment located in Boulder, CO every 5 seconds. |
| 1.11 | EDOS shall provide SCS (spacecraft summary session) summary reports to the ICESat Flight Operations Segment located in Boulder, CO after each spacecraft contact. |
| 1.12 | EDOS shall deliver a data file containing Star Tracker, IRU, LRS, and GPS packets to Flight Dynamics Facility (FDF) within 6 hours of receipt of downlink at a GSIF |
| 1.13 | EDOS shall distribute physical media containing archived GLAS PDSs to the ISIPS located at the Wallops Flight Facility upon request(D3 tapes). |
| 1.14 | EDOS shall provide processing support for ICESat low rate data that are played back from the spacecraft recorder. |
| 1.15 | EDOS shall provide Reed-Solomon (Grade of Service III) decoding on the ICESat low rate return link data as required. |
| 1.16 | EDOS shall provide rate buffered delivery service for ICESat low rate return link data. |
| 1.17 | EDOS shall receive schedules for downlink support from the ICESat Control Center located in Boulder, CO |
| 1.18 | EDOS shall receive, create, and deliver all external data products including schedules, rate buffered data, EDSs, PDSs, CODA reports, and SCS summary reports, in conformance with the EDOS-EGS Elements ICD. |
| 1.19 | EDOS shall deliver PDSs and EDSs to the ISIPS system located at the Wallops Flight Facility. |
| 1.20 | EDOS shall archive all GLAS Production Data Sets (PDSs) on physical media (D3 tapes) at the Data Archive Facility (DAF) located at White Sands, New Mexico. |

## EDOS ICESat Mission Performance Reqirements

| 2.1 | EDOS shall provide frame synchronization for ICESat high rate return link data at rates up to 40 Mbps from one physical channel. |
| --- | --- |
| 2.2 | EDOS shall provide processing support to produce GLAS PDSs from single spacecraft contact sessions at the average incoming data rate of 500 kbps per orbit. |
| 2.3 | EDOS shall provide processing support to produce GLAS EDSs from single spacecraft contact sessions for selected data at the average data volume of 2% of production data set volume. |
| 2.4 | EDOS shall deliver GLAS PDSs to the GSFC DAAC, within 24 hours of receipt of all appropriate input data at GSFC. |
| 2.5 | EDOS shall deliver GLAS EDSs to the GSFC DAAC, within 3 hours of receipt of all appropriate input data at GSFC. |
| 2.6 | EDOS shall provide frame synchronization for ICESat low rate return link playback data at rates up to 262.144 kbps from one physical channel. |
| 2.7 | The LZPF shall initiate the transfer of rate buffered data to a destination within 5 minutes after receipt of all of the data for the rate buffering session. |
| 2.8 | The LZPF shall have an MTTRes of 2 hours or less for all functionality required to support non-real-time mission data handling. |
| 2.9 | The LZPF shall have an operational availability of 0.998 or greater to support non-real-time mission data handling. |

## Data Products Latency Requirements

The following table summarizes the latency requirements for S-band and X-band data.

### Calibration & Validation Phase Expedited Data

During the calibration & validation phases (~L+120 days), select science products shall be delivered to the ISF within 1 hour of receipt at the ground station.

### Flight Dynamics X-band Data Products

The EDOS shall extract and deliver to the FDS the GPS data packets within 6 hours of X-band contact to the Flight Dynamics Facility.

# Science Data Processing

Perform Science Data Processing in accordance with the GLAS Science Software Requirements Document.

- Receive Level Zero Data Products from the LZDP facility.

- Produce Level 1 and Level 2 Standard Data Products.

- Deliver Level 1 and Level 2 Standard Data Products to the Science Data Archive & Distribution Facility.

# Science Data Archival & Distribution

## NSIDC DAAC

- Accept Level 0 production data sets from EDOS.

- Accept Level 1 and Level 2 Standard Data Products from the ISIPS Facility.

- Provide a permanent archive of Level 0, Level 1 and Level 2 data products.

- Maintain a Database of all data products in the Archive.

- Update the Archive and the Database when reprocessed products are delivered.

- Accept requests from the user community for specific data products.

- Distribute data products to the user community as requested.

# Spacecraft Contractor Requirements

## Engineering Data Archive

BASD shall maintain a permanent archive of all spacecraft  engineering data, including schematics, specifications, operations manuals and drawings that are necessary to trouble-shoot and maintain the spacecraft during on-orbit operations.  This data archive is to be maintained at BASD under configuration management for the life of the mission.

## Integration & Testing Activities

BASD shall schedule support for the following major ground system tests.

| GSCT # | S/C Activity – ICEsat | Approximate Month/Year |
| --- | --- | --- |
| #1: Basic Tlm, command | S/C Bus performance Test | 4/00 |
| #2: RF Tlm, CMD | Transmitter, SSR with CTV | 6/00 |
| #3: Instrument Ops | Post electrical Integration CPT/APT | 12/00 |
| #4: Full ETE Dry Run | Post Thermal Vac | 1/01 |
| #5: Full ETE | Post Thermal Vac | 2/01 and 4/01 |
| #6: Launch Site ETE | Align SFF | 6/01 |
| #7: Pad ETE | Payload Aliveness and ESDIS | 7/00 |

## Sustaining Engineering Support

### Anomaly Resolution

BASD shall provide anomaly resolution support to resolve any Observatory anomalies that may occur from launch through mission end-of-life (EOL).  This includes supporting the development of any Observatory operating contingencies resulting from unplanned changes in the mission operations baseline (e.g., changes in orbit, power, subsystem degradation, etc.) and to support the resolution of anomalies such as software errors, out of tolerance parameters, etc., and providing expert consultation to the FOT.

### Trending & Analysis

BASD shall provide capabilities to trend and analyze key Observatory parameters.  This includes any trending or analysis of  the Observatory’s  operating and health & safety conditions, especially when needed in support of anomaly resolution.  This also includes trending and analysis to support planned Observatory flight configuration changes, including raising from calibration to mission orbit, transition to first full eclipse season, and executing required yaw transitions.

### Software Maintenance

BASD shall provide FSW maintenance.  This shall include the maintenance of development and test beds and providing expertise to modify, test, and deliver any uploadable FSW or parameters that may be required during mission life.

NOTE:  Although FSW source code shall be delivered to the government, the government shall not modify any FSW code.

### Maintain Flight Software Test Bed

The provisions for the Flight Software Test Bed (FSTB) shall be as follows:

- The FSTB shall remain resident at BASD to EOL.

- The FSTB shall be dedicated to the ICESat mission to EOL, meaning that the ICESat FSTB shall not be used for any other spacecraft developments.

- The FSTB shall be accessible for off-line FOT training and FSW validation purposes with the MOC on a scheduled basis to EOL.

- BASD shall maintain the FSTB to EOL.

- BASD shall remain technically cognizant and technically competent in the operation of the ICESat FSW and the FSTB to EOL.

# GLAS Instrument Developer Requirements

Code 924, the GLAS Instrument Developer, shall provide the following functions and services to support the ICESat operations.

## Instrument Operations Training

Code 924 shall provide training for the Instrument Operations Team (IOT) and Flight Operations Team (FOT)  personnel in instrument operations and maintenance.  This shall include the development of written training materials, providing formal classroom training, and on-the-job training (OJT) during instrument and observatory Integration & Test (I&T) to a level deemed sufficient by the organizations to be trained to transfer operational knowledge of the GLAS Instrument to these operations personnel.

Classroom Training

Code 920 shall provide formal classroom training to the IOT and the FOT.  This shall include a video taped session, training materials, and documentation.

On the Job Training (OJT)

At the GLAS I&T facility at GSFC, the IOT and FOT shall have access to the GLAS instrument in an observation capacity during key phases of the GLAS I&T process.  These observation sessions shall serve to familiarize the IOT/FOT with the flight hardware.

## Documentation

Code 920 shall provide operations documentation that includes:

- GLAS Operations Manual

- GLAS Flight Software Manual

## Integration & Testing Activities

Code 924 shall participate in end-end science data flow tests with the ground system prior to launch.  This includes supporting any simulations and dress rehearsals for the analysis of instrument science and engineering data, and to support the development of the Science Computing Facility (SCF) for instrument operations and science data processing, and to support the development of the MOC/FOT for nominal observatory level operations.

## On-Orbit Check-out & Transition Activities

- Code 924 shall support the on-orbit check-out and transition phases.

- Code 924 shall provide personnel to be resident at the MOC to support the FOT/IOT during on-orbit check-out of the ICESat bus and the GLAS instrument.

- Code 924 personnel shall monitor telemetry and approve all commands sent to the Observatory during this phase.

## Calibration and Validation Support

Code 924 shall support the Calibration and Validation (C&V) Phase.  C&V support includes analysis and evaluation of on-orbit GLAS performance.

## Engineering Data Archive

- Code 924 shall maintain a GLAS Engineering Data Archive to includes all schematics, specifications, operations manuals, drawings, and test results that are necessary to trouble-shoot and maintain the instrument during on-orbit operations.

- This archive shall to be maintained under configuration management for the life of the mission.

## Instrument Sustaining Engineering

Code 924 shall provide the following sustaining engineering functions for the life of the ICESat mission.

### Anomaly Resolution Support

Code 924 shall provide Anomaly Resolution Support to resolve any GLAS Instrument anomalies that may occur from launch through mission end-of-life (EOL).  This includes supporting the development of any instrument operating contingencies resulting from unplanned changes in the mission operations baseline (e.g., changes in orbit, power, subsystem degradation, etc.) and to support the resolution of anomalies such as software errors, out of tolerance parameters, etc., and providing expert consultation to the IOT/FOT.

### Trending & Analysis

Code 924 shall provide Trending & Analysis of key GLAS parameters.  This includes any trending or analysis of GLAS operating and health & safety conditions, especially when needed in support of anomaly resolution.  This also includes trending and analysis to support planned GLAS flight configuration changes (such as laser switching or altimetry detector switching) and any calibration and validation support required to support these activities.

### Software Maintenance

Code 924 shall provide GLAS Flight Software (GFSW) Maintenance.  This includes maintaining GFSW development and test beds and providing expertise to modify, test, and deliver any uploadable FSW or parameters that may be required during mission life.

# Science Team Requirements

Calibration & Validation

MODIS Overflights

Need inputs from Science Team…

# Appendices

## Acronyms

AD	Attitude Determination

AGS	Alaska Ground Station

AOS	Acquisition of Signal

BAP	Baseline Activity Plan

BASD	Ball Aerospace Systems Division

C&V	Calibration & Validation

CCSDS	Consultive Committee for Space Data Systems

CMD	Command

CTV	Compatibility Test Van

DAAC	Distributed Active Archive Center

Delta V	Delta Velocity (budget)

DMR	Detailed Mission Requirements

DSU	Data Storage Unit

Ebnet	EOSDIS Backbone Network

EDOS	EOS Data and Operations System

EOC	EOS Operations Center

EOL	End-of-Life

EOS	Earth Observing System

EOSDIS	EOS Data Information System

EPGS	EOS Polar Ground Station

ESDIS	Earth Sciences Data Information Systems

ETE	End-to-End

FDR	FDS Design Review

FDS	Flight Dynamics System

FDSTP	FDS Test Plan

FEICD	FDS External Interface Control Document

FMECA	Failure Modes and Effect Analysis

FOT	Flight Operations Team

FOV	Field of View

FRR	Flight Readiness Review

FSTB	Flight Software Test Bed

FSW	Flight Software

FTP	File Transfer Protocol

G&N	Guidance & Navigation

GFSW	GLAS Flight Software

GLAS	Geoscience Laser Altimeter System

GPS	Global Positioning System

GSCT	Ground System Compatibility Test

GSEF	GLAS Sustaining Engineering Facility

GSFC	Goddard Space Flight Center

GSMF	GLAS Software Maintenance Facility

HVAC	Heating, Ventilation, and Cooling

I&T	Integration & Test

ICD	Interface Control Document

ICESat	Ice, Cloud, and Land Elevation Satellite

IGS	ICESat Ground System

IOT	Instrument Operations Team

IRU	Inertial Reference Unit

ISF	Instrument Support Facility

ISF	Instrument Support Facility

ISIPS	ICESat Science Investigator Processing System

Kbps	Kilo Bits Per Second

km	Kilometers

LASP	Laboratory for Astronomy and Solar Physics

LRR	Launch Readiness Review

LZDP	Level Zero Data Processing

Mbps	Mega Bits Per Second

MDR	Mission Design Review

MOC	Missions Operations Center

MODIS

MOR	Mission Operations Review

MORD	Mission Operations Requirements Document

MOSR	Mission Operations Status Review

NASA	National Aeronautics & Space Administration

NISN	NASA Integrated Support Network

NSIDC	National Snow & Ice Data Center

OA	Operational Attitude

OASIS	Operations and Science Instrument Support

OD	Orbit Determination

OJT	On-the-Job Training

OOD	Operational Orbit Determination

ORR	Operations Readiness Review

PB	Playback (data)

PDS	Production Data Sets (EDOS)

POD	Precision Orbit Determination

R/T	Real Time (data)

RF	Radio Frequency

S/C	Spacecraft

SCC	Spacecraft Control Computer

SCF	Science Computing Facility

SLR	Satellite Laser Ranging

SOMO	Space Operations Management Office

SSEF	Spacecraft Sustaining Engineering Facility

SSR	Solid State Recorder

SSST	Solid State Star Tracker

ST	Science Team

TBD	To be Determined

Tlm	Telemetry

TT&C	Tracking, Telemetry & Control

UT	University of Texas

WFF	Wallops Flight Facility

WGS	Wallops Ground Station

WOTIS	Wallops Orbital Tracking Information System

## Critical Requirements Allocation Matrix