UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON D.C., 20460

OFFICE  OF

PREVENTION, PESTICIDES AND

TOXIC SUBSTANCES

PC Code: 268800

DP Barcode: D328740

April 26, 2006

MEMORANDUM

SUBJECT:		Drinking Water Assessment for the IR-4 registration for the new uses of         dimethomorph for use on brassica head and stem subgroup 5A.

TO:			Barbara Madden, Risk Manager Reviewer

Daniel Rosenblatt, Risk Manager

Registration Division (7505P)

AND:			John Redden, Team Leader

Technical Review Branch

Registration Division (7505P)

FROM:		José Luis Meléndez, Chemist

Environmental Risk Branch V

Environmental Fate and Effects Division

THROUGH:		Karen Whitby, Acting Branch Chief

Environmental Risk Branch V

Environmental Fate and Effects Division (7507P)

This memo presents the Tier I Estimated Surface Drinking Water Concentrations and Estimated Ground Water Concentrations (EDWCs) for Dimethomorph, calculated using the Tier I aquatic models FIRST and SCI-GROW, respectively, for use in the human health risk assessment.

The Estimated Drinking Water Concentrations (EDWCs) for dimethomorph were calculated based on a maximum application rate of 1.4 lb a.i./A/season.  The acute drinking water concentration in surface water is 81.1 ppb of dimethomorph, based on applications of the chemical to broccoli (representative of brassica head and stem).  The cancer/chronic drinking water concentration is 24.7 ppb (based on applications to broccoli, highest application rate).  The SCI-GROW generated EDWC is 0.264 ppb of dimethomorph, which is recommended for use, both for acute and chronic exposures.  Table I provides a summary of the Tier I modeled drinking water concentrations.  Should there be a need for additional refinements, the EFED can perform a Tier II aquatic assessment, for surface waters.

EXECUTIVE SUMMARY

Dimethomorph’s full chemical name is (E,Z) 4-[3-(4-chlorophenyl)-3-(3,4-dimethoxyphenyl)-1-oxo-2-propenyl] morpholine, CAS# 110488-70-5, and PC code 268800.  The CAS# for the E diatereoisomer is 113210-97-2.  The CAS# for the Z diastereoisomer is 113210-98-3.  Its’ structure has three rings, two of which are phenyl-type rings (refer to structure in Appendix D).

Dimethomorph is a systemic fungicide which protects plants from molds, as well as killing molds on plants and preventing their spread. It is a cinnamic acid derivative and a member of the morpholine chemical family.  It’s mode of action is the inhibition of sterol (ergosterol) synthesis.  It is a mixture of two isomers (E and Z) but only the Z isomer has fungicidal activity. It is available as a wettable powder.  The use proposed in this IR4 (Interregional Research Project No. 4) is brassica head stem and stem subgroup 5A.  It is to be applied as a foliar spray.

This is a Tier I screening drinking waters assessment using Tier I aquatic models SCI-GROW and FIRST, and maximum application rates for dimethomorph, with minimum interval between applications.  It was found that the worst case scenario was brassica head and steam group (represented by broccoli) for dimethomorph, with the highest seasonal application rate, and the highest PCA.  There were no major degradates observed in the aerobic soil metabolism study; therefore, no degradates were modeled in this exercise.  Should additional refinements of the assessment are needed, the EFED can schedule a higher Tier analysis.

There are uncertainties in this assessment related to the mobility studies.  Three studies are available, but two of them were conducted with foreign soils.  They indicated more mobility than the study conducted with domestic soils.  Furthermore, the metabolism studies showed high levels of nonextractable residues.  At this time, it appears that there are no terrestrial field dissipation studies, to confirm what happened in the laboratory.

The proposed use involved in this action is for the following IR4 tolerance petition:  brassica head and stem, subgroup 5A.  It includes broccoli, Chinese broccoli, Brussels sprouts, cabbage, Chinese cabbage {napa}, Chinese mustard, cauliflower, cavalo broccoli and hohlrabi (refer to highlighted section of Table 2 for additional details).

Table 1.  Maximum Tier I Estimated  Drinking Water Concentrations (EDWCs) for drinking water  risk assessment based on aerial application of dimethomorph.

| DRINKING WATER SOURCE (MODEL USED) | USE (rate modeled) | MAXIMUM ESTIMATED DRINKING WATER CONCENTRATION (EDWC) (ppb) |
| --- | --- | --- |
| Groundwater (SCIGROW) | Broccoli (1.4 lb a.i./A) | Acute and chronic | 0.264 |
| Surface water (FIRST) | Broccoli (1.4 lb a.i./A) | Acute | 81.1 |
|  | Broccoli (1.4 lb a.i./A) | Chronic | 24.7 |

PROBLEM FORMULATION

This is a Tier I drinking water assessment that uses modeling to estimate the groundwater and surface water concentrations in drinking water source (pre-treatment), resulting from pesticide use on sites that are highly vulnerable. This initial tier screens out chemicals with low potential riskand allows OPP to focus resources on more refined risk assessments for chemicals which potentially present more significant risks. This drinking water assessment will report potential exposure concentrations for the human health dietary risk assessment and provide a clear and transparent description of how those concentrations were determined.

ANALYSIS

Use Characterization

Table 2 is a summary of all agricultural use patterns for dimethomorph.  The highlighted use is the proposed new one under IR4 petition.  The use information was obtained from the current label for ACROBAT® 50WP Fungicide, and the proposed label for the same product.

Table 2.  Summary use information for dimethomorph, based on ACROBAT® 50WP Fungicide label (EPA Reg. No. 241-410), containing 50.0% a.i., and 50.0% inerts.

| USE | SINGLE APP RATE (lb a.i./A) | NO. OF APPS. | SEASONAL APP. RATE (lb a.i./A) | INTERVAL BETWEEN APPS. (days) | APP. METHOD | INCORPORATION DEPTH (inches) |
| --- | --- | --- | --- | --- | --- | --- |
| Bulb Vegetable (Garlic, leek, onion, shallot) | 0.2 | 5 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Cucurbit vegetable (chayote, cantaloupe, Chinese waxgourd, citron melon, cucumber, gherkin, edible gourd, momordica spp., muskmelon, pumpkin, squash, winter watermelon, summer squash) | 0.2 | 5 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Fruiting vegetable group (except tomato) (eggplant, ground cherry, pepino, pepper, tomatillo) | 0.2 | 5 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Leafy brassica greens | 0.2 | 5 | 1.0 | 7 | Ground, aerial, chemigation | 0 |
| Hops | 0.2 | 3 | 0.6 | 10 | Ground, aerial, chemigation | 0 |
| Lettuce (head and leaf) | 0.2 | 5 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Potato | 0.2 | 5 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Taro | 0.2 | 5 | 1.0 | 7 | Ground, aerial, chemigation | 0 |
| Tobacco | 0.25 | 4 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Tomato-Non-staked | 0.2 | 5 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Tomato-Staked | 0.2 | 5 | 1.0 | 5 | Ground, aerial, chemigation | 0 |
| Brassica, head and stem, subgroup 5A (broccoli, Brussels sprouts, cabbage, Chinese cabbage {napa}, Chinese mustard, cauliflower, cavalo broccolo, hohlrabi | 0.2 | 7 | 1.4 | 7 | Ground, aerial, chemigation | 0 |

ACROBAT® 50WP Fungicide is a wettable powder.  It may be applied by ground methods, chemigation, or aerially.  There are no buffer zone restrictions in this label.  Usually the maximum seasonal application rate is 1.0 lb a.i./A.  For the proposed new use (IR4 petition), the maximum seasonal application rate is 1.4 lb a.i./A.  Thorough coverage is required to obtain maximum benefit and minimize the potential for resistance.

The use pattern selected for drinking water modeling was the proposed new use (brassica head and stem), and the representative crop was broccoli.  It was selected because it involves the maximum application rate, and hence, the maximum exposure.  Furthermore, it has the maximum PCA (the default of 0.87).

Fate and Transport Characterization

Table 3 provides a detailed summary of physical/chemical and environmental fate/transport properties of dimethomorph, including measured parameters, values, data sources, and comments.

Table 3.  Summary of physical/chemical and environmental fate and transport properties of dimethomorph.

| PARAMETER | VALUES (s) (units) | SOURCE | COMMENT |
| --- | --- | --- | --- |
| Chemical Name | 4-[3-(4-chlorophenyl)-3-(3,4-dimethoxyphenyl)-1-oxo-2-propenyl]morpholine (EZ)-4-[3-(4-chlorophenyl)-3-(3,4-dimethoxyphenyl)acryloyl] morpholine | – | CAS name IUPAC name |
| Molecular Weight | 387.86 | – | – |
| Solubility (20ºC) | E isomer: at pH 5 13 mg/L, at pH 7 12 mg/L, at pH 9 11 mg/L Z isomer: at pH 5 6 mg/L, at pH 7 6 mg/L, at pH 9 5 mg/L | -- | – |
| Melting Point | 127-148ºC | Tomlin (ed.) | Z isomer169.2-170.2ºC E isomer135.7-137.5ºC |
| Bulk Density | 1318 Kg/m3 | Tomlin (ed.) | -- |
| Solubility (20-23ºC) (g/L) | Acetone: 15 (Z), 88 (E); cyclohexanone 27(Z); dichloromethane 315 (Z); dimethylformamide 40 (Z), 272 (E); hexane 0.02 (Z), 0.04 (E); methanol 7 (Z); toluene 7 (Z) | Tomlin (ed.) | _ |
| Vapor Pressure (20ºC) | E isomer 7.3 x 10-9 mmHg Z isomer 7.5 x 10-9 mmHg | Tomlin (ed.) | – |
| Henry’s Law Constant | 2.06-2.13 x 10-10 atm-m3/mole | -- | Estimated from vapor pressure and water solubility. |
| pKa (20ºC) | Not available | -- | – |
| Octanol-Water Partition Coefficient Kow, at 20º | 479 | Tomlin (ed.) | log KOW = 2.68 |
| Hydrolysis Half-life (pH 4, 7, 9 [70 or 90ºC]) | stable | MRID: 43917226. | Stable at all pHs for a period of 10 weeks. |
| Aquous Photolysis Half- life (pH 5) | t1/2 = 50-56 days | MRID: 43917227. | Value corresponds to 12 hour photocycle in midsummer, uncorrected half-life with continuous irradiation was 25-28 days. |
| Soil photolysis half- life | t1/2 = 75 days | MRID: 43917228. | Continuous irradiation with a xenon arc lamp. |
| Aerobic Soil Metabolism Half-life | t1/2 = 66 days t1/2 = 117 days | MRID: 43917229, 43917230. | Study yielding a half-life of 66 days was deemed supplemental. Both studies were performed with foreign soils (British, German). |
| Anaerobic Soil Metabolism Half-life | DT50 ~ 5-10 days DT50 < 20 days t½ = 26.2 and 25.7 days | MRID 43917231, 43917232, 44780201 | Supplemental studies; system was dosed with Lucerne meal when the flasks were made anaerobic. Other study also supplemental. |
| Anaerobic Aquatic Metabolism Half-life | <1 day <1 day | MRID: 43917233. | Supplemental studies. |
| Aerobic Aquatic Metabolism Half-life | Not Available | NA | -- |
| Organic Carbon Partition Coefficient (KOC) | 566, 402, 290, 515, 377, 388, 316, 1588, 1158, 1485, 787 mL/gOC | MRID: 46235734, 43917235, 44780202. | Various foreign soils, two soils tested twice (once in each study). The last four readings were performed with domestic soils (acceptable). |
| Soil Partition Coefficient (Kd) | 4.47, 11.67, 2.09, 4.94, 8.51, 2.72, 3.03, 15.7, 10.1, 19.0, 11.9 mL/g |  |  |
| Terrestrial Field Dissipation Half-life | Not available | NA | -- |

The major routes of dissipation of dimethomorph appear to be metabolism, which is moderate (66-117 days aerobic and around 26 days anaerobic).  Another possible route of dissipation is leaching, since 5 out of the 11 Kd values were less than 5.  Based on the FAO mobility classification, the KOC values range from moderately mobile to slightly mobile.  Dimethomorph can reach adjacent bodies of water via spray drift or through runoff dissolved in the water or partly adsorbed to eroding particles depending on the properties of the soil.  Dimethomorph has some potential to be persistent, however there are uncertainties in the database that do not allow one to reach concrete conclusions.

One aspect of dimethomorph is that the diastereoisomer that is active is the Z one.  In the last anaerobic soil metabolism and in the aqueous photolysis studies, it was observed that there was conversion of the E isomer to the Z isomer (the one that is active). This phenomenon could have an impact in the assessments if the Z isomer is more toxic than the E isomer.

There is also uncertainty with respect to the formation of transformation products.  In the aerobic soil metabolism no major transformation products were detected but large amounts of unextracted material were observed.  In the last anaerobic soil metabolism study (supplemental), two transformation products were observed:  p-desmethyl dimethomorph and m-desmethyl dimethomorph.  No information on any other transformation product could be gathered and no degradation pathway could be traced for dimethomorph.

There is also uncertainty with respect to two mobility studies that were deemed supplemental because they were conducted with foreign soils.  These studies yielded smaller Kd‘s and KOC‘s than the study conducted with domestic soils.

Dimethomorph is not likely to bioaccumulate substantially in fish or other aquatic organisms as indicated by its low octanol/water partition coefficient (479).

Table 4.  Summary of degradate formation from degradation of dimethomorph

| STUDY TYPE | SOURCE | DEGRADATE and MAXIMUM CONCENTRATION |
| --- | --- | --- |
|  |  | p-desmethyl dimethomorph (% applied) | m-desmethyl dimethomorph (% applied) | DEG3 (% applied) |
| Hydrolysis | MRID: 43917226. | -- | – | – |
| Aqueous Photolysis | MRID: 43917227. | -- | -- | – |
| Soil Photolysis | MRID: 43917228. | -- | -- | – |
| Aerobic Soil Metabolism | MRID: 43917230, 43917229. | -- | – | – |
| Anaerobic Soil Metabolism | MRID: 43917231, 43917232. | Observed | Observed | -- |
| Aerobic Aquatic Metabolism | Not Available | -- | – | – |
| Anaerobic Aquatic Metabolism | MRID: 43917233. | -- | – | – |
| Terrestrial Field Dissipation | Not Available | -- | – | – |

Drinking Water Exposure Modeling

Models

SCI-GROW (Screening Concentration in Ground Water) is a regression model used as a screening tool for ground water used as drinking water.  SCIGROW was developed by regressing the results of Prospective Ground Water studies against the Relative Index of Leaching Potential (RILP).  The RILP is a function of aerobic soil metabolism and the soil-water partition coefficient.  The output of SCI-GROW represents the concentrations that might be expected in shallow unconfined aquifers under sandy soils, which is representative of the ground water most vulnerable to pesticide contamination likely to serve as a drinking water source.  (Ref. 2)

FIRST (FQPA Index Reservoir Screening Tool) is a screening model designed by the Environmental Fate and Effects Division (EFED, 2001a) of the Office of Pesticide Programs to estimate the concentrations found in drinking water from surface water sources for use in human health risk assessment.  As such, it provides upper bound values on the concentrations that might be found in drinking water due to the use of a pesticide.  FIRST is a single event model (one runoff event), but can account for spray drift from multiple applications.  Spray drift (resulting in direct deposition of the pesticide into the reservoir) is assumed to be 16% of the applied active ingredient for aerial application, 6.3% for orchard air blast application, and 6.4% for other ground spray application.  FIRST is hardwired to represent the Index Reservoir, a standard water body used by the Office of Pesticide Programs to assess drinking water exposure (Office of Pesticide Programs, 2002).  It is based on a real reservoir (albeit not currently in active use as a drinking water supply), Shipman City Lake in Illinois, that is known to be vulnerable to pesticide contamination. The single runoff event moves a maximum of 8% of the applied pesticide into the reservoir.  This amount can be reduced due to degradation on the field and the effects of binding to soil in the field.  FIRST also uses a Percent Cropped Area (PCA) factor to adjust for the area within the watershed that is planted to the modeled crop.  The default agricultural PCA is 0.87.  (Ref. 3 and 4)

For volatile and semi-volatile compounds, Tier I modeling will tend to over-estimate EDWCs because there are no parameters in SCI-GROW and FIRST that explicitly take into account volatility (ie., no vapor pressure input).  Therefore, in reality, more of the compound will be volatilizing than Tier I can account for.  If drinking water levels of concern are exceeded for over-estimated Tier I EDWCs, Tier II modeling will be able to refine these EDWCs by including volatility considerations.

Modeling Approach and Input Parameters

Table 5 provides the input parameter values used for modeling of dimethomorph using SCI-GROW.  Table 6 provides the input parameter values used for modeling of dimethomorph using FIRST.  As indicated earlier, no degradates were included in the modeling because none exceeded 10% of the applied in the aerobic soil metabolism study.

There were three batch equilibrium studies yielding 11 Kd‘s and KOC‘s.  Two studies were conducted with foreign soils and yielded lower K values than the study conducted with domestic soils.  The lowest non-sand Kd was selected (as opposed to the KOC).   Of the two solubilities (one for the Z and for the E isomers), the highest one was selected.  Since there was no aerobic aquatic metabolism data and the chemical is stable to hydrolysis, twice the input for the aerobic soil metabolism was used.  In general, the EFED guidance for the selection of input parameters for FIRST and SCI-GROW was used.  The new version of FIRST V1.1.0 was utilized.

The Percent Cropped Area (PCA) used in this drinking water assessment was 0.87.  It is the default value for “other crops” for which there is no PCA.  It is also the maximum PCA available.

Table 5. SCI-GROW (v2.3) input parameter values for dimethomorph use on broccoli1.

| PARAMETER (units) | VALUE(S) | SOURCE | COMMENT |
| --- | --- | --- | --- |
| Maximum Application Rate (lb a.i./A) | 0.2 | Label ACROBAT® WP Fungicide. | – |
| Number of Applications per Year | 7 | Label ACROBAT® WP Fungicide. | Represents most-conservative scenario with the maximum number of applications. |
| Organic Carbon Partition Coefficient (Koc; mL/g) | 515 | MRID: 43917234, 43917235, 44780202. | Median value out of 11 available. It is noted that there is more than a five-fold difference in the range. |
| Aerobic Soil Metabolism Half-life (days) | 91.5 | MRID: 43917229, 43917290. | Average value of two available (117 and 66 days) |

1 Parameters are selected as per Guidance for Selecting Input Parameters in Modeling the Environmental Fate and Transport of Pesticides; Version II, February 28, 2002.

Table 6. FIRST (v1.0) input parameter values for dimethomorph use on broccoli1.

| PARAMETER (units) | VALUE(S) | SOURCE | COMMENT |
| --- | --- | --- | --- |
| Application Rate (lb a.i./A) | 0.2 | Label ACROBAT® WP Fungicide. | – |
| Number of Applications | 7 | Label ACROBAT® WP Fungicide. |  |
| Interval between Applications (days) | 7 | Label ACROBAT® WP Fungicide. |  |
| Percent Cropped Area (decimal) | 0.87 | Proposed label. | National default. |
| Soil Partition Coefficient [Kd; (mL/g) or KOC (mL/gOC)] | 3.03 | MRID: 43917234, 43917235, 44780202. | Represents the lowest non-sand Kd value among eleven values ranging from 2.09 to 19.0 mL/g. |
| Aerobic Soil Metabolism Half-life (days) | 147 | MRID: 43917229, 43917230. | Represents the 90th percentile of the upper confidence bound on the mean of two half-life values: 117 and 66 days; mean 91.5 days, std. dev, 25.5 |
| Wetted in? | No | Label ACROBAT® WP Fungicide. | – |
| Depth of Incorporation (inches) | 0 | Label ACROBAT® WP Fungicide. | – |
| Method of Application | Aerial spray | Label ACROBAT® WP Fungicide. | – |
| Solubility in Water @ 20 OC, unbuffered (mg/L or ppm) | 12 | _ | At pH 7 the solubility of the Z isomer is 12 mg/L and the E isomer is 6 mg/L; the maximum value was used. |
| Aerobic Aquatic Metabolism Half-life (days) | 294 | MRID: 43917229, 43917230 | No aerobic aquatic metabolism data are available and the pesticide is hydrolytically stable. 2X the aerobic soil metabolism half-life input value is used. |
| Hydrolysis Half-life @ pH 7 (days) | 0 | MRID: 43917226. | Stable. |
| Aquatic Photolysis Half-life @ pH 7 (days) | 56 | MRID: 43917227. | – |

1 Parameters are selected as per Guidance for Selecting Input Parameters in Modeling the Environmental Fate and Transport of Pesticides; Version II, February 28, 2002

Modeling Result

Table 7.  Maximum Tier I Estimated Drinking Water Concentrations (EDWCs) for drinking water risk assessment based on aerial application of dimethomorph.

| DRINKING WATER SOURCE (MODEL USED) | USE (rate modeled) | MAXIMUM ESTIMATED DRINKING WATER CONCENTRATION (EDWC) ( ppb) |
| --- | --- | --- |
| Groundwater (SCIGROW) | Broccoli (1.4 lb a.i./A) | Acute and Chronic | 0.264 |
| Surface water (FIRST) | Broccoli (1.4 lb a.i./A) | Acute | 81.1 |
|  | Broccoli (1.4 lb a.i./A) | Chronic | 24.7 |

SCI-GROW concentration (ppb) represents the groundwater concentration that might be expected in shallow unconfined aquifers under sandy soils. Output is used for both acute and chronic endpoints.

FIRST concentrations (ppb) represent untreated surface water concentrations.

The peak day concentration (over 30 years) is used for acute endpoints and the annual average concentration (over 30 years) is used for chronic endpoints.

The estimated concentrations provided in this assessment are conservative estimates of concentrations in drinking water.  If dietary risks require refinement, higher tiered crop-specific and location-specific models and modeling scenarios can be utilized.

Monitoring Data

Monitoring data usually provide different kinds of information than modeling (e.g., monitoring reflects current use pattern, underestimates frequency of occurrence, often misses peaks, inputs cannot be adjusted as modeled ones can, usually done for purposes other than characterizing exposure from a particular pesticide), and, consequently, tend to complement the modeling rather than refine it.  In general, a useful interpretation of monitoring values requires in-depth assessment of the data, which is beyond the scope of a Tier I assessment.

Drinking Water Treatment

There are no data available on the effects of water treatment on the possible increasing dissipation and/or the transformation into products that may be less or more toxic than the parent. (Ref. 6)

CONCLUSIONS

In this assessment it has been assumed that the reported value is the total dimethomorph (Z + E isomers).  The results yielded an acute estimated surface water concentration of 81.1 ppb and a cancer/chronic drinking water concentration of 24.7 ppb.  The groundwater EDWC, suitable for acute and chronic exposure is 0.264 ppb.

Several uncertainties surround the environmental fate database utilized in this assessment.  Several of the studies were deemed supplemental and discrepancies were observed as described earlier in the summary of the environmental fate.

APPENDIX A.  References

- Policy Establishing Current Versions of Exposure Models and Responsibility for Model Maintenance (11/06/2002)

- SCIGROW: Users Manual (11/01/2001, revised 08/23/2002)

- FIRST Users Manual (08/01/2001)

- FIRST: A Screening Model to Estimate Pesticide Concentrations in Drinking Water (05/01/2001)

- Guidance for Selecting Input Parameters in Modeling the Environmental Fate and Transport of Pesticides, Version II (02/28/2002)

6	The Incorporation of Water Treatment Effects on Pesticide Removal and Transformations in Food Quality Protection Act (FQPA) Drinking Water Assessments  (10/25/2001)

- Tomlin, CDS (ed.) The Pesticide Manual-World Compendium, 11th edition, British Crop Protection Council, Surrey, England 1997, p. 416

- Food and Agriculture Organization of the United Nations.  FAO PESTICIDE DISPOSAL SERIES 8.  Assessing Soil Contamination: A Reference Manual.  Appendix 2.  Parameters of pesticides that influence processes in the soil.  Editorial Group, FAO Information Division: Rome, 2000 [ http://www.fao.org/DOCREP/003/X2570E00.htm ]

Appendix B.  SCI-GROW Output File

SCIGROW

VERSION 2.3

ENVIRONMENTAL FATE AND EFFECTS DIVISION

OFFICE OF PESTICIDE PROGRAMS

U.S. ENVIRONMENTAL PROTECTION AGENCY

SCREENING MODEL

FOR AQUATIC PESTICIDE EXPOSURE

SciGrow version 2.3

chemical:Dimethomorph

time is  4/19/2006  11:47:19

------------------------------------------------------------------------

Application      Number of       Total Use    Koc      Soil Aerobic

rate (lb/acre)  applications   (lb/acre/yr)  (ml/g)   metabolism (days)

------------------------------------------------------------------------

0.200           7.0           1.400      5.15E+02       91.5

------------------------------------------------------------------------

groundwater screening cond (ppb) =   2.64E-01

************************************************************************

Appendix C.  FIRST Output File

RUN No.   1 FOR Dimetomorph      ON   Broccoli      * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL   APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL     Kd   (PPM )    (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

.200(  1.271)   7   7       3.0   12.0   AERIAL(16.0)  87.0      .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

147.00        2          N/A     56.00- 6944.00   294.00    282.06

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB)) Ver 1.1.0 DEC 12, 2005

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

81.144                     24.736

Appendix D.  Molecular Structure of Dimethomorph