Exhibit(400)-130.7

TIGTA SIGARMS Armorer’s Maintenance Log Sheet

P228    P226    P239    SN: __________________    Division:_______________    Page:____

Firearm Assigned to Special Agent: ______________________________  POD: ________________

Discuss with Special Agent and estimate the of # of rounds fired since last maintenance:_____

Reason maintenance performed: Annual Inspection  Other  (If Other, explain below.)

________________________________________________________________________________________________________

Maintenance performed, action taken, and results:

____________________________________________________

________________________________________________________________________________________________________

Were "Chicago Upgrade" Parts previously installed on this firearm: Yes   No

(If yes, complete and attach the SIG UPGRADE/REBUILD CHECK SHEET)

Did you install the "Chicago Upgrade" Parts : Yes   No  (If no, explain why in Remarks.)

Parts inspection completed: Yes   No  (See list below.)

Function test completed: Yes   No  (See page two.)

Test fired: Yes   No

Cleaned: Yes   No

Was a temporary firearm issued to Special Agent: Yes   No

(If yes, provide model _____ and serial number:_____________________and dates:________to______)

Remarks:

________________________________________________________________________________________________________

----------------------------------------------------------------------------------------------------

Date Maintenance Completed: _____________ Armorer: ________________________

Date Armorer Certification Expires : ________

Test fired by: ________________________

Location:_______________________________________________________Date: ________

---------------------------------------------------------------------------------------------------------------------

Parts Inspection: (Confirm serviceability by checking after you inspect each part/grouping.)

Slide - Ejection port, locking surfaces, arresting notch for the slide catch lever, finish.  ___

Barrel - bore and chamber, locking surfaces, feed ramp, muzzle. ___

Recoil spring and recoil spring guide. ___

Extractor. ___

Firing pin and firing pin spring - projection of the firing pin through the breech face. ___

Pins H.D. of the breechblock – replace. ___

Safety lock and safety lock spring. ___

Front and rear sights - nightsights clean and work, tightness of fit. ___

B.  Frame – finish. ___

Take-down lever. ___

Locking insert & slide catch lever spring. ___

Trigger, trigger pivot pin, trigger bar, and trigger bar spring. ___

Decocking lever, bearing, and spring. ___

Slide catch lever. ___

Ejector. ___

Sear, sear spring and safety lever. ___

Hammer, hammer stop, reset spring. ___

Hammer strut assembly. ___

Magazine catch. ___

Magazine catch support plate. ___

Grip plates, grip plate screws. ___

C.  Magazine - tube and lips, finish. ___

Floorplate. ___

Insert. ___

Spring. ___

Follower. ___

Function Inspection

Trigger and Hammer Mechanism

1.  Decocking Lever

Clear the pistol.

Cock the hammer.

Place moderate pressure on the back of the hammer to ensure positive sear engagement with the hammer.

Thumb down the decocking lever and check that the trigger returns to the double action position.

Check that the hammer has come to rest in the safety intercept notch before reaching the extreme dropped position.

2.  Double action function

With hammer decocked, pull the trigger.

Check that the hammer moves to the rear, drops forcefully and rebounds to the safety intercept notch after striking the firing pin.

3.  Interruption of trigger function or disconnector operation

With hammer forward and the trigger retained to the rear, pull the slide to the rear and release it.

Check that the hammer is retained in the cocked position (trigger remains pulled).

4.  Single-action function

Release the trigger.

Check that the trigger bar engages the safety lever once more and, that upon pulling the trigger again, the hammer is released.

B.  Recoil Spring

Check the force of the recoil spring and smooth cycling of the slide.

Carry out the loading movement and check that the slide/barrel group springs forward smartly and locks.  Repeat once.

C.  Magazine

Check the condition of the magazine tube, the lips and the floorplate.

Check for correct interlocking of the floorplate and insert.

Check for smooth movement and springing of the magazine follower.

Check for ease of insertion of the magazine into the frame and positive locking.

Check for free in and out movement of the magazine catch.

With an empty magazine in place, pull the slide to the rear and release it - the slide must be arrested in the rear position by the slide catch lever.

D.  Slide Catch Lever

Thumb down the slide catch lever and check that the slide is released and forcefully springs forward.

Thumb down the decocking lever.

SIG UPGRADE/REBUILD CHECK SHEET

Replace ALL of the parts listed below.  Check the Replaced block for each item replaced and attach this sheet.

Part

Number       Description	Replaced

228 Parts Diagram #

9         34226031  MODIFIED BREECHBLOCK	___

(RETURN OLD PART TO NFC.)

2         34280075  Guide, Recoil Spring (hollow)               ___

3         34225490  Recoil Spring	___

7         34221650  Inner Pin H.D.	___

8         34221600  Outer Pin H.D.	___

10       34222030  Extractor                                               ___

11       34260530  Firing Pin	___

12       34221560  Spring, Firing Pin	___

13       34225580  Safety Lock                                           ___

14       34225590  Spring, Safety Lock	___

19       34280080.01  Spring, Slide Catch Lever	___

23       34260242  Spring, Trigger Bar	___

25       34221070  Spring, Sear	___

27       34221090  Spring, Pin H.D.	___

34       34225688  Main Spring (10 LB.)	___

35       34221200  Spring, Pin	___

37       34225190  Hammer stop	___

38       34225390  Spring, Reset	___

42       34221040  Spring, Decocking Lever	___

45       34225210  Spring, Magazine Catch	___

46       34225220  Magazine Catch Stop	___

47       34225230  Spring, Magazine Stop	___

34260640 Grip Screws  	___

(Replace if damaged.)

52       34260640  Magazine Spring	___  Number replaced___

REPLACE ONLY IF DAMAGED, AND REPLACEMENT PARTS ARE AVAILABLE

34260631  Followers, Law enforcement mags

___Number replaced___

54       34280215    Floorplates, Law enforcement magazines, P-228

___ Number replaced___

226 Parts Diagram #

2          34260510  Guide, Recoil Spring (226)	___

3          34260540  Recoil Spring (226)	___

19        34225160  Spring, Slide Catch lever (226)       ___

SIGHT REPLACEMENT

6     34260565_08  Replacement rear night sight	___

5     34260555_08  Replacement front night sight	___

Sight in firearm.  ___

Armorer Signature __________________________and Date Work Completed_______