| Area/Facility Description Title: Research Support Building [BNL-FRA-01] Area/Facility # (if applicable): Building 400 | Point Value → Parameter ↓ | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- |
| Area/Facility Description: Office building with administrative offices, meeting rooms, public areas, lunch rooms, Credit Union, and mechanical equipment support areas. | Occupancy or Use (A) | <once/year | <once/month | <once/week | <once/shift | >once/shift |
| Name(s) of Risk Team Members: FRA development team: R. Selvey (SHSD), N. Bernholc (SHSD), P. Martino (F&O), D. Dowling (HR), P. Sparrow (IA), N. Gmur (NSLS), R. Backofen (PA), R. Colichio (DJ) Building Walk-down of controls: R. Selvey (SHSD), N. Bernholc (SHSD), P. Martino (F&O), P. Sparrow (IA), R. Backofen (PA), Joann Giambalvo (SS), J. Torre (EP). | Severity (B) | First Aid Only | Medical Treatment | Lost Time | Partial Disability | Death or Permanent Disability |
| Approved by: N. Bernholc SORD OSH Representative Date: 2/09/07 Rev.#: Final Rev0 | Likelihood (C) | Extremely Unlikely | Unlikely | Possible | Probable | Multiple |
| Reason for Revision (if applicable): | Comments: |

| Physical Item or Activity | Hazard(s) | Without Controls |  | Risk with Controls in Place |  | Risk with Additional Controls in Place |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Occupancy A | Severity B | Likelihood C | Risk* AxBxC | Control(s) | Occupancy A | Severity B | Likelihood C | Risk* AxBxC | Control(s) Added to Reduce Risk Or Comment/Unresolved Issue | Occupancy A | Severity B | Likelihood C | Risk* AxBxC | % Risk Reduction |
| Walking into and from building | Falls, falls to a slightly lower level (curb), bodily reaction | 5 | 3 | 3 | 45 | Proper lighting, handrails by stairs/ramps; Photocells on outdoor lights; handicap parking spaces provided with ramps and markings | 5 | 3 | 2 | 30 |  |  |  |  |  |  |
| Walking on rain, ice, snow covered surfaces | Slips, trips, and falls (contusions, fractures, broken bones, back injuries) | 5 | 4 | 4 | 80 | Mats at entrances; Application of salt on icy walking surfaces, “Snowflake” designation for increased emphasis by grounds crew, drainage at water collection points, grounds maintenance, delayed opening of BNL, wearing appropriate footwear | 5 | 3 | 2 | 30 |  |  |  |  |  |  |
| Parking | Struck by Vehicle | 5 | 4 | 5 | 100 | Marked walkways/crosswalks, curbs, proper lighting, use speed limits | 5 | 2 | 3 | 30 |  |  |  |  |  |  |
|  | Vehicle collide or strike object- injury to occupants | 5 | 3 | 4 | 60 | Marked parking lanes, traffic flow markings, speed limits and enforcement | 5 | 2 | 3 | 30 |  |  |  |  |  |  |
| Walking inside building | Slips, trips, and falls, fall to lower level (stairs) | 5 | 4 | 3 | 60 | Lighting, building maintenance and custodial services, stair treads and handrails, high traction tiles, Tier I inspections, general housekeeping by residents | 5 | 2 | 3 | 30 |  |  |  |  |  |  |
|  | Blocked routes of egress in emergencies | 5 | 5 | 2 | 50 | Tier I inspections, general housekeeping, Normal and battery backup emergency lighting, life safety code, proper planning and layout of office equipment, Tier I inspection. | 5 | 5 | 1 | 25 |  |  |  |  |  |  |
|  | Walking into Glass doors and walls | 5 | 2 | 3 | 30 | Glass etching to make walls more visible | 5 | 2 | 2 | 20 |  |  |  |  |  |  |
| Using elevators | Falls to same level due to uneven alignment at doors; stuck inside during failed operation of lift | 4 | 3 | 2 | 24 | Proper lighting and emergency lighting, elevator maintenance, elevator inspections, Tier 1 inspections, call buttons in elevator; fail safe design of elevator | 4 | 3 | 1 | 12 |  |  |  |  |  |  |
| Escape- if overcrowding of CR1&2 meeting rooms | Injury in egress during emergencies | 3 | 4 | 2 | 24 | Exits marked, Multiple egress windows at ground level; Dual door exits from room. | 3 | 4 | 1 | 12 |  |  |  |  |  |  |
| Security | Security hazards associated with working alone and/or late at night; isolated areas such as basement | 4 | 3 | 3 | 36 | Adequate lighting, buddy system, working door locks, escort service, on-site Police with 911/222 access | 4 | 3 | 1 | 12 |  |  |  |  |  |  |
| Indoor air quality | Allergies, asthma, headaches, pulmonary exposure from communicable diseases and occupant activities in common/cubicle areas; irritation from new building materials | 4 | 3 | 2 | 30 | Building maintenance, periodic changing air filters from HVAC | 5 | 2 | 1 | 10 |  |  |  |  |  |  |
| Inadequate Lighting | Falls to same level | 5 | 2 | 4 | 40 | SHSD conducted a walkthrough and observed adequate lighting levels for egress during day and for office work efficiency. | 5 | 2 | 1 | 10 |  |  |  |  |  |  |
| Noise | Exposure to hazardous noise levels | 5 | 3 | 1 | 30 | Normal operations do not include high noise equipment or activities. Noise survey to be done per SBMS if occupant equipment and/or activities are at unacceptable levels | 5 | 1 | 1 | 5 |  |  |  |  |  |  |
| General Fire Hazards | Fire Hazards | 4 | 4 | 4 | 64 | Fire extinguishers, fire alarms, water sprinklers, Tier I inspections, building maintenance, general housekeeping to reduce combustibles, SBMS fire safety subject area | 4 | 2 | 2 | 16 |  |  |  |  |  |  |
| Fire and Safety at electrical Distribution panels | Blocked panels preventing access in emergencies | 5 | 3 | 1 | 15 | Tier 1 Inspections, marked floor | 5 | 1 | 1 | 5 |  |  |  |  |  |  |
| Office Storage | Being struck by an object | 5 | 3 | 3 | 45 | Limit usage of top shelves above head, lower shelf heights, Tier 1 Inspections | 5 | 2 | 2 | 20 |  |  |  |  |  |  |
| Office shelving | Falling items | 5 | 2 | 4 | 80 | Limit usage of top shelves, lower shelf height, limit weight of objects stored on shelves, Tier I inspections. | 5 | 2 | 1 | 10 |  |  |  |  |  |  |
| Kitchen/Lunch room heating of foods | Thermal burns from hot appliances food items- centralized kitchens, transporting food to desks | 5 | 3 | 3 | 45 | No gas or electric stoves, microwave only, GFCI plugs at wet locations | 5 | 2 | 2 | 20 |  |  |  |  |  |  |
| Credit Union Service Area | Routine entry of office areas by families with small children for banking | 5 | 3 | 3 | 45 | General safety features of building designed without “attractive nuisances”; parental control | 5 | 2 | 1 | 10 |  |  |  |  |  |  |
| (Non-ionizing Radiation sources) | Thermal burns | - | - | - | - | No known sources | - | - | - | - |  |  |  |  |  |  |
| (Ionizing Radiation sources) | Adverse health impact- neoplasms or burns | - | - | - | - | No known sources | - | - | - | - |  |  |  |  |  |  |
| (Asbestos in building components) | Inhalation of fibers with adverse health effects | - | - | - | - | None- building designs and specification prohibited installation during construction | - | - | - | - |  |  |  |  |  |  |

| Further Description of Controls Added to Reduce Risk or Issues for further investigation: Issue that may need to be addressed during the occupancy phase of the building: Issue #1 May need a JRA for outside window cleaning as this building has large amount of exterior glass Issue#2: Finance/Payroll office security measures may block second means of egress Issue #3: Physical security & access during filing in basement- personal security. SSD suggested resolution: Controls could include: Informing others of your location (I'm going downstairs to file), going in pairs (buddy system), adding access control measures (card readers, camera assessment, etc). For the access control measures, this would have to be decided/request by the Building Manager. Issue #4: Lighting survey needed for evening light levels for occupant work efficiency. Issue #5: Noise Survey needed after occupancy if sources are introduced. Issue #6: Deficiencies noted in the ORE. Item #7: Indoor Air Quality complaints from initial occupants on irritated eyes, headaches, dryness, too hot, too cold. [SHSD S&H Rep conducted investigation]. Item #8: Ergonomic setup for the supervisor and staff personnel on standard issue furniture. [SHSD Ergonomist investigated on case by case basis]. Item #9: Exterior rooms do not have window shades [On order]. |
| --- |
| *Risk: | 0 to 20 | 21 to 40 | 41-60 | 61 to 80 | 81 or greater |
|  | Negligible | Acceptable | Moderate | Substantial | Intolerable |