(A)     		                    P R I M A R Y   C H A R A C T E R I Z A T I O N   D A T A

S74-Ark-121-6-(1-8), 74RO06   (RANDOLF COUNTY, ARKANSAS)                              SOIL CHARACTERIZATION LABORATORY

AGRONOMY DEPARTMENT

SAMPLED AS: GEPP                                                         		UNIVERSITY OF ARKANSAS

REVISED TO:                                                         		FAYETTEVILLE, ARKANSAS 72701

--------- ---------------------------------------------------------------------------------------------------------------

(- - -TOTAL - - -) (- - - - -SILT- - - - - -)   (- - - -  - -SAND- -  - - - )  (TEXTURE)

CLAY  SILT  SAND   FINE  	MEDIUM	COARSE 	  VF     F     M     C    VC

SAMPLE     DEPTH   HORIZON     LT   .002  .05    .002    .005	.02	 .05   .10   .25    .5     1

NO.      (IN)               .002  -.05   -2    -.005    -.02	-.05	 -.10  -.25  -.50   -1     -2

<- - - - - - - - - - - - - -PCT OF <2MM  (3A1)- - - - - - - - - - - - - ->

none	  ½-0	O1

7875       0- 1   	A1        11.7  70.6  17.7     9.9     28.9	31.8	 5.8   4.9   2.5   3.3   1.2     sil

7876       1- 7   	A2        14.2  63.3  22.5    12.1     31.7 	19.5	 9.2   5.0   3.4   2.8   2.1     sil

7877       7-13   	A&B       26.5  56.5  17.0    12.3     25.7 	18.5	 6.8   4.1   2.7   1.8   1.6     sil

7878      13-28   	B21T      70.2  24.4   5.4     8.3      8.6	 7.5	 2.8   1.0   0.6   0.7   0.3      c

7879      28-41   	B22T      76.5  19.5   4.0     4.5      8.2	 6.8	 1.5   0.8   0.5   0.7   0.5      c

7880      41-53   	B22T      76.5  19.4   4.4     5.5      6.8	 7.1	 1.4   1.0   0.5   0.9   0.6      c

7881      53-63   	B3T       83.1  13.8   3.1     3.0      6.1	 4.7	 1.0   0.6   0.3   0.7   0.5      c

7882      63-72   	B3T       82.3  13.6   4.1     0.4      8.0	 5.2	 1.5   0.7   0.6   0.8   0.5      c

--------- -------------------------------------------------------------------------------------------------------------

ORGN (- BULK DENSITY -)        (- - - NH4OAC EXTRACTABLE BASES-  - - -)  ACID-      BASE   (- - - -PH - - -)

M     FIELD  1/3  OVEN         CA     MG        NA       K        SUM   ITY       -SAT    KCL   CACL2  H2O

DEPTH	        MOIST  BAR  DRY						        NH4OAC  IN   .01M

(IN)	 6A1c   4A3a  4A1d  4A1h         5B5a  5B5a      5B5a    5B5a       5c3   6H5a       5C1    8C1g  8C1f  8C1f

PCT    <- - - G/CC- - ->      <- - - - - - - - - - - MEQ / 100 G- - - - - - ->       PCT	    1:2  1:1

½-0	  -                               -       -        -  	  -        -     -           -                  -

0- 1     1.50                            7.5     1.2      0.2	 0.3      9.2   12.2	43	         6.3

1- 7     0.30                            1.2     0.2      0.2	 0.2      1.8    7.2	20	         5.4

7-13     0.20                            1.0     0.4      0.2	 0.2      1.8    6.2	23	         5.3

13-28     0.10                            2.6     3.0      0.2	 0.3      6.1   15.9	28	         5.1

28-41     0.10                            2.4     3.5      0.2	 0.4      6.5   19.8	25	         5.0

41-53     0.10                            2.0     3.7      0.2	 0.4      6.3   18.0	26	         5.0

53-63     0.10                            1.9     3.2      0.2	 0.4      5.7   22.6	20	         5.1

63-72     0.10                            1.9     3.2      0.2	 0.4      5.7   22.5	20	         5.1

(B)                                N A R R A T I V E   P E D O N   D E S C R I P T I O N

Pedon: Gepp    Soil Survey Number S74-Ark-121-6-(1-8), 74RO06    Location: SESESW,S11,T21N,R03W

Latitude: ____     Longitude: ____    Physiography: ____    Geomorphic Position: ____    Microrelief:____

Erosion or Deposition: ____    Slope: 12-20%    Elevation:____    Precipitation:____    MLRA: N/A    Water Table Depth:____

Permeability: ____    Air Temperature:____    Drainage: ____    Land Use: wooded     Stoniness:____     Runoff: ____

Particle Size Control Section: ____   Parent Material:____    Classification: ____    Diagnostic Horizons: ____

Described by: Brown and McFadden    Sample Date: ____

O1 – partly decomposed orgnic matter; not sampled

A1 --  0 to  1 in; dark grayish brown cherty (50%) silt loam; weak fine granular structure; very friable; common fine and medium roots; few worm holes and castings; pH 6.0; abrupt smooth boundary. 7875

A2 -- 1 to  7 in; yellowish brown (10YR 5/4) cherty (40%) silt loam; weak medium subangular blocky structure; friable; common fine and medium roots; few worm holes; few pores; pH 5.5; clear,wavy boundary.  7876

A&B -– 7 to 13 in; yellowish red (5YR 4/8) silty clay loam; streaks of yellowish brown (10YR 5/4) and (10YR 5/6) silt loam; weak medium subangular blocky structure; friable; about 10% chert fragments from 1/8 in to 3 in in diameter; few fine and few medium roots; few pores; pH5.0; clear smooth boundary.  7877

B21t -– 13 to 28 in; red (2.5YR 4/8) clay; moderate to strong medium subangular blocky structure breaking to strong fine angular blockky structure; firm; continuous thin clay films on faces of peds; few (<5%) chert fragments; few roots; few pores; pH 4.5; gradual smooth boundary.  7878

B22t -– 28 to 53 in; red (2.5YR 4/8) clay; common fine and medium faint red (10YR 4/8), yellowish red (5YR 4/8) and common medium distinct strong brown (7.5YR 5/8) mottles; moderate to strong medium subangular blocky structure; firm continuous thin clay films on faces of peds; about 5% chert fragmments from ½ to 3 in diameter; few pores lined with clay films; few medium roots; pH 5.0; gradual smooth boundary.  7879 (28 to 41 in), 7880 (41 to 53 in)

B3t – 53 to 72 in; yellowish red (5YR 4/8) clay; common medium distinct strong brown (7.5YR 5/8), common medium prominent red (10YR 4/6) and few fine prominent light gray (10yR 7/1, 7/2) mottles; moderate to strong subangular blocky structure breaking too strong fine angular blocky structure; firm; continuous thin clay films; about 10% chert and siltstone fragments up to 3 in diameter; pH 5.5.  7881 (53 to 63 in), 7882 (63 to 72 in)